Creating ASM65.COM
------------------
Thå ASM6µ assembleò haó beeî builô aó aî overlaù tï Digitaì �
Research'ó ASÍ assembleò foò 808° serieó processors® Tï protecô �
youò CP/Í licencå froí Digitaì Research¬ ASM6µ ió supplieä onlù �
iî .HEØ form¬ anä musô bå mergeä witè aî existinç copù oæ ASM.COÍ �
usinç DDÔ oò á similaò 8080/Z8° debugger® Usinç DDT¬ thå �
conversatioî tï creatå ASM65.COÍ ió aó follows:

     A>ddt asm.com
     DDT VERS 2.2
     NEXT  PC
     2100 0100
     -iasm65.hex
     -r
     NEXT  PC
     2300 0100
     -^C
     A>save 34 asm65.com



ŠBackground
----------
ASM6µ ió á 650² cross-assembleò foò CP/Í systemó -- iî otheò �
wordó iô useó 650² assemblù languagå tï creatå programó foò 6502-�
baseä systems¬ buô thå assembleò itselæ runó oî CP/Í systems¬ �
allowinç thå uså oæ better-qualitù editoró sucè aó WordStaò anä �
Spellbindeò tï creatå prograí source® Iô ió á fulì conditionaì �
buô non-macrï assembleò supportinç alì 650² opcodeó anä �
addressinç modeó (includinç thå extensionó supporteä oî thå GTÅ �
65C0² processor© witè á gooä rangå oæ pseudo-operations® Iô doeó �
NOT converô 8080/Z8° assemblù languagå programó tï 650² �
equivalents.

Wå assumå thaô yoõ arå familiaò witè assemblù languagå �
programminç -- iæ not¬ wå woulä adviså readinç '650² Assemblù �
Languagå Programming§ (Leventhal¬ Osborne/McGraw-Hill© oò aî �
equivalenô iî conjunctioî witè theså notes® Wå alsï assumå thaô �
yoõ havå á copù oæ thå Digitaì Researcè ASÍ manuaì tï hand¬ aó wå �
wilì refeò tï iô foò descriptionó oæ pseudo-ops¬ erroò messageó �
anä thå like.

Iî general¬ thå assemblù languagå useä iî ASM6µ followó standarä �
MOÓ Technologù syntax¬ buô therå arå somå deviationó froí thå �
standarä (enforceä bù usinç aó corå aî assembleò designeä foò thå �
8080/Z8° processoò family© whicè maù affecô portabilitù oæ �
programó tï standarä 650² assemblers® Thå maiî differenceó arå iî �
thå specificatioî oæ numeriã valueó (in suffixeó ratheò thaî �
prefixeó arå useä tï distinguisè numbeò bases)» iî pseudo-oð �
names¬ whicè arå standarä ASÍ syntax; anä iî thå descriptioî oæ �
indirecô addressinç modes® Bracketó arå useä tï encloså �
arithmetiã expressionó iî ASÍ syntax¬ witè thå resulô thaô �
indirecô addressinç modeó cannoô bå specifieä bù enclosinç thå �
operanä iî bracketó aó peò MOÓ Technologù syntaø -- onå non-�
standarä opcodå (JMPI© anä slightlù differenô registeò mnemonicó �
(IX¬ IÙ anä I© arå useä instead.

Preparing source files
----------------------
Prograí creatioî witè ASM6µ ió á three-stagå process: editinç thå �
sourcå filå witè á suitablå editoò oò word-processor» usinç ASM6µ �
tï creatå á heø file» anä creatinç á binarù filå froí thå heø �
filå witè LOAÄ oò CODE¬ oò sendinç iô direcô tï thå externaì �
6502-baseä system® Thió parô oæ thå noteó ió concerneä onlù witè �
the first stage, that of source-file creation.

Programó caî bå createä usinç anù suitablå CP/Í editoò oò word-�
processoò (wå mainlù uså WordStar¬ whicè allowó uó sourcå fileó �
oæ anù length)® Filenameó MUST uså thå extensioî .A6µ (e.g® �
PROGRAM.A65)¬ otherwiså ASM6µ wilì noô finä thå filå -- thå erroò �
message 'No source file present' will be printed in this case.

As usual, assembly language statements take the form of:

     <label:> opcode <operand> <;comment>

-- eacè linå ends¬ oæ course¬ witè carriage-returî oò thå CR/LÆ �
combination.Š
Linå numberó shoulä noô bå useä (thougè seå thå ASÍ manuaì foò �
more detail if you REALLY want to use line numbers).

Labels
------
Labeló maù bå oæ anù length¬ althougè onlù 1¶ characteró arå �
significant® Theù maù bå writteî aó eitheò uppeò oò loweò caså �
letteró (lower-caså letteró arå converteä tï capó automaticallù �
durinç assembly© anä numeraló (althougè thå firsô characteò oæ á �
labeì musô bå á letter® Thå ':§ ió optional® Wherå á labeì referó �
tï aî assignmenô (EQÕ oò SET© iô musô bå oî thå samå line» �
otherwise¬ wherå iô referó tï codå (opcodeó oò code-creatinç �
pseudo-opó sucè aó DB© iô doeó noô neeä tï bå oî thå samå line¬ �
sï thaô multiplå labeló maù refeò tï thå samå codå location® Seå �
the ASM manual for more detail.

Multiple expressions
--------------------
Opcodeó anä operandó arå describeä iî detaiì below¬ anä wilì noô �
bå discusseä here® Note¬ however¬ thaô severaì opcode/operanä �
expressionó maù bå placeä oî thå samå line if separated by '!':

     PHA ! TXA ! PHA ! TYA ! PHA   ;save registers

-- onå side-effecô ió thaô '!§ maù noô bå useä iî comments¬ �
otherwiså ASM6µ interpretó thå followinç texô aó sourcå �
statements, with unpredictable results.

Comments
--------
Á commenô ió precedeä bù ';'¬ anä runó tï thå enä oæ thå linå �
(witè thå exceptioî oæ '!§ aó describeä above)® Therå ió nï �
provisioî foò multiple-linå commentó -- eacè linå oæ commenô musô �
bå precedeä bù ';§ -- althougè commentó maù starô aô anù positioî �
in the line.

Eacè parô oæ thå statemenô musô bå separateä bù aô leasô onå �
spacå oò tab® Aparô froí this¬ spaceó anä tabó arå noô �
significant¬ anä maù bå useä iî anù waù tï increaså thå �
readability of the file.

Opcodes
-------
ASM6µ supportó alì standarä MOÓ Technologù anä GTÅ (65C02© opcodå �
mnemonics¬ witè onå exceptionº JMPÉ ió useä iî placå oæ JMÐ (..© �
foò jump-indirect® Witè thaô exception¬ alì opcodå mnemonicó arå �
three-letter» thå four-letteò mnemonicó ASLA¬ ROLA¬ LSRA¬ RORÁ �
(anä INCA¬ DECÁ -- 65C0² only© maù alsï bå useä tï describeä �
accumulator operations.

Thå opcodå lisô belo÷ showó alì oæ thå opcodeó availablå witè �
ASM65¬ includinç 65C0² extensions® Thå addressinç modeó availablå �
foò eacè instructioî arå showî iî brackets¬ witè modeó availablå �
onlù oî thå 65C0² indicateä bù aî asterisk® Thå modeó arå �
repesented by:
     (none)    implicit operation
     A         accumulator only
     #         immediate (8-bit value)Š     Z         zero page (8-bit address)
     Abs       absolute (16-bit address)
     Rel       relative (8-bit signed branch)
     Z,X       zero page + X register
     Z,Y       zero-page + Y register
     Abs,X     absolute + X register
     Abs,Y     absolute + Y register
     IX        indirect from (zpage + X register)
     IY        indirect from zpage, + Y register
     I         indirecô froí zpagå (samå aó IÙ witè Y=0© (65C0² �
               only)

Implicit operations
-------------------
     PHA, PLA       push/pull accumulator
     PHP, PLP       push/pull processor status flags
     PHX, PLX       push/pull X register (65C02 only)
     PHY, PLY       push/pull Y register (65C02 only)
     TSX            move stack pointer to X register
     TXS            set stack pointer from X register
     TAX, TAY       load X, Y register from A
     TXA, TYA       load A from X, Y register
     SEC, SED, SEI  set carry, decimal, interrupt flags
     CLC, CLD       clear carry, decimal flags
     CLI, CLV       clear interrupt, overflow flags
     RTS, RTI       return from subroutine, interrupt
     BRK            break (software interrupt)
     NOP            no-operation

Call, Jump and Branch
---------------------
     JSR            call subroutine (Abs)
     JMP            jump to new location (Abs)
     JMPI           jumð indirecô viá specifieä locatioî (Abs» �
                    Abs,X*)
     BPL, BMI       branch if sign clear/set (Rel)
     BNE, BEQ       branch if zero flag clear/set (Rel)
     BCC, BCS       branch if carry clear/set (Rel)
     BVC, BVS       branch if overflow flag clear/set (Rel)
     BRA            unconditional branch (Rel*)

Test/Set/Reset memory
---------------------
     BIT            test memory bits (Z; Abs; Z,X*; Abs,X*; #*)
     TRB            tesô anä reseô memorù againsô accumulatoò �
                    (Z*» Abs*)
     TSB            tesô anä seô memorù againsô accumulatoò (Z*» �
                    Abs*)

Rotate and Shift
----------------
     ASL            shift left (Z; Abs; Z,X; Abs,X; A)
     ASLA           shift A left (same as ASL A)
     LSR            shift right (Z; Abs; Z,X; Abs,X; A)
     LSRA           shift A left (same as LSR A)
     ROL            rotatå lefô -- 9-biô rotatå througè carrù (Z» �
                    Abs» Z,X» Abs,X» A)
     ROLA           rotate A left (same as ROL A)
     ROR            rotatå righô -- 9-biô rotatå througè carrù �Š                    (Z» Abs» Z,X» Abs,X» A)
     RORA           rotate A right (same as ROR A)

Decrement and Increment
-----------------------
     DEC            decrement (Z; Abs; Z,X; Abs,X; A*)
     DECA           decrement A (same as DEC A*)
     INC            increment (Z; Abs; Z,X; Abs,X; A*)
     INCA           increment A (same as INC A*)
     DEX, INX       decrement/increment X
     DEY, INY       decrement/increment Y

Accumulator operations
----------------------
     ORA            inclusivå OÒ witè accumulatoò (#» Z» Abs» �
                    Z,X» Abs,X» Abs,Y» IX» IY» I*)
     AND            binarù ANÄ witè accumulatoò (#» Z» Abs» Z,X» �
                    Abs,X» Abs,Y» IX» IY» I*)
     EOR            exclusivå OÒ witè accumulatoò (#» Z» Abs» �
                    Z,X» Abs,X» Abs,Y» IX» IY» I*)
     ADC            adä witè carrù tï accumulatoò (#» Z» Abs» �
                    Z,X» Abs,X» Abs,Y» IX» IY» I*)
     SBC            subtracô witè borro÷ froí accumulatoò (#» Z» �
                    Abs» Z,X» Abs,X» Abs,Y» IX» IY» I*)

Load and Store
--------------
     LDA            loaä Á registeò (#» Z» Abs» Z,X» Abs,X» �
                    Abs,Y» IX» IY» I*)
     STA            storå Á registeò (Z» Abs» Z,X» Abs,X» Abs,Y» �
                    IX» IY» I*)
     LDX            load X register (#; Z; Abs; Z,Y; Abs,Y)
     STX            store X register (Z; Abs; Z,Y)
     LDY            load Y register (#; Z; Abs; Z,X; Abs,X)
     STY            store Y register (Z; Abs; Z,X)

Compare registers
-----------------
     CMP            comparå accumulatoò (#» Z» Abs» Z,X» Abs,X» �
                    Abs,Y» IX» IY» I*)
     CPX            compare X (#; Z; Abs)
     CPY            compare Y (#; Z; Abs)

Addressing modes
----------------
(none)    implicit operation
A         accumulator only
               Useä wherå accumulatoò ió thå operand¬ e.g® ASÌ A® �
               Alì Á addressinç optionó havå á 4-letteò matchinç �
               opcode -- i.e. ASLA and ASL A are identical.
#         immediate (8-bit value)
               Nexô bytå ió thå operand® Exampleó arå LDÁ #20¬ �
               LDØ #20h¬ CPØ #'i'® Aî erroò ió generateä iæ thå �
               operand evaluates to greater than 0FFh.
Z         zero page (8-bit address)
               Nexô bytå ió thå low-ordeò addresó oæ thå operand® �
               Selecteä automaticallù iæ thå operanä evaluateó tï �
               lesó thaî 100h® Exampleó arå LDÁ 20¬ STØ 20h¬ anä �
               ORA <address> where <address> is less than 100h.
               Alì zero-pagå addresseó musô bå knowî oî thå firsô �Š               pass¬ withouô forwarä references¬ otherwiså phaså �
               erroró (seå ASÍ manual© maù occuò durinç thå �
               second pass of the assembler.
Abs       absolute (16-bit address)
               Nexô bytå ió thå low-ordeò addresó oæ thå operand» �
               followinç bytå ió thå high-ordeò address® Selecteä �
               automaticallù iæ thå operanä evaluateó tï greateò �
               thaî 0FFh¬ oò iæ zero-pagå modå ió noô available® �
               Exampleó arå LDÁ 2000¬ STØ 200h¬ anä ORÁ <address> �
               where <address> is greater than 0FFh.
Rel       relative (8-bit signed branch)
               Nexô bytå ió thå offseô tï á labeì relativå tï thå �
               starô oæ thå NEXT instructioî (i.e® twï byteó �
               afteò thå locatioî oæ thå brancè test)¬ givinç aî �
               effectivå rangå oæ -12¶ tï +12¹ froí thå locatioî �
               oæ thå brancè instruction® Iæ thå operanä �
               evaluateó outsidå thió range¬ aî erroò wilì bå �
               generated® Exampleó arå BRÁ label¬ BNÅ $-³ ('$§ ió �
               the reserved name of the position counter).
Z,X       zero page + X register
               Aó foò Ú above¬ excepô thå contentó oæ thå Ø �
               registeò arå addeä tï givå aî offseô withiî thå �
               zero-page® Addresseó 'wrað round§ WITHIN zero-�
               page. Example: AND address,X
Z,Y       zero-page + Y register
               Aó foò Z,Ø above¬ excepô thaô thå Ù registeò ió �
               used. Example: STX 20h,Y
Abs,X     absolute + X register
               Aó foò Abó above¬ excepô thaô thå contentó oæ thå �
               Ø registeò arå addeä tï givå aî offseô froí thå �
               followinç two-bytå address® Addresseó dï noô 'wrað �
               round§ withiî thå currenô pagå -- wherå thå suí oæ �
               thå low-ordeò addresó anä thå Ø registeò contentó �
               exceedó 0FFh¬ thå high-ordeò addresó ió �
               incremented. Example: SBC 2000h,X
Abs,Y     absolute + Y register
               Aó foò Abs,Ø above¬ excepô thaô thå Ù registeò ió �
               used® Exampleº ADÃ address,Ù (wherå addresó ió �
               greater than 0FFh).
IX        indirect from (zpage + X register)
               Thå followinç bytå ió thå lo÷ ordeò addresó withiî �
               zero-pagå tï whicè thå Ø registeò ió addeä �
               ('wrappinç round§ iæ necessary)® Thå effectivå �
               operanä ió thå addresó pointeä tï by thå contentó �
               oæ thå effectivå addresó generated® Iæ thå baså �
               addresó doeó noô evaluatå tï aî 8-biô addresó �
               (i.e® thå high-ordeò bytå ió greateò thaî zero© �
               an error is generated. Example: LDA base,IX
IY        indirect from zpage, + Y register
               Similaò tï IX¬ excepô thaô thå contentó oæ thå Ù �
               registeò arå addeä AFTER thå indirectioî -- thå �
               contentó oæ thå Ù registeò arå addeä tï thå �
               contentó oæ thå twï byteó aô 'address§ (withiî �
               zero-page© tï creatå thå effectivå address® Iæ thå �
               baså addresó doeó noô evaluatå tï aî 8-biô addresó �Š               an error is generated. Example: CMP 20h,IY
I         indirecô froí zpagå
               Thå effectivå addresó ió thå contentó oæ thå twï �
               byteó startinç aô thå followinç addresó iî zero-�
               page® Thió ió identicaì tï IÙ iî caseó wherå thå Ù �
               register is zero. Example: AND flag,I

Twï otheò addressinç modeó arå available¬ buô onlù witè thå JMÐ �
instructionº absolutå indirect¬ anä absolutå indexeä indirect® �
Theså arå availablå aó JMPÉ Abó anä JMPÉ Abs,Ø respectively» thå �
JMP instruction has only the Abs addressing mode.

Numeric values
--------------
(Noteº Thió ió NOT thå samå aó MOÓ Technologù syntax)® Fouò �
numbeò baseó arå recognisedº binary¬ octal¬ decimaì anä �
hexadecimal® Theså arå representeä bù thå followinç suffixes:

     B         binary -- 011011b
     O or Q    octal -- 377q
     D         decimal (defaults to decimal) -- 100, 100d
     H         hexadecimal -- 20h, 0FFh

Alì numeriã valueó MUST starô witè á numbeò -- heø valueó abovå �
9Fh must be prefixed by 0.

Numeriã valueó arå treateä aó 16-biô unsigneä numbers» thå �
addressinç modå useä checkó thaô thå numbeò ió withiî itó �
required range.

Arithmetic expressions
----------------------
Operandó maù includå arithmetiã expressionó oæ considerablå �
complexity® Thå followinç ió á lisô oæ thå functionó anä �
operatoró thaô maù bå useä withiî arithmetiã expressions®

     * times
     + plus
     - minus
     / divide
     MOD remainder from divide
     & binary AND (note -- not 'AND', which is a 6502 opcode)
     OR binary inclusive-OR
     XOR binary exclusive-OR
     NOT binary negate
     SHL binary shift-left
     SHR binary shift-right   

Alì arithmetiã operationó acô oî thå currenô valuå aó á 16-biô �
unsigneä number® Bracketó -- ¨ © -- encloså theså expressionó anä �
maù bå nesteä uð tï siø deep» bracketó caî alsï bå useä tï forcå �
thå ordeò oæ evaluatioî oæ aî expression® Seå thå ASÍ manuaì foò �
morå details.

Literal expressions
-------------------
Texô (oò individuaì letters© maù bå includeä iî operandó bù �
enclosinç it in single quotes, e.g.:Š
     CMP #'T'
     db   'text'

Wherå single-quoteó characteró arå tï bå included¬ theù musô bå �
repeated:

     db   'it''s a little confusing'
     CMP #''''      ;is A single-quote?

For more details, see the ASM manual.

Pseudo-operations
-----------------
Pseudo-opó falì intï fivå groupsº defininç oò reservinç space¬ �
defininç constantó oò variables¬ defininç thå locatioî counter¬ �
delimitinç areaó foò conditionaì assembly¬ anä (aó yeô �
unimplemented© expansioî instructions® Onlù á brieæ summarù ió �
given here: for more detail refer to the ASM manual.

Defining space
--------------
DB   definå bytå (equivalenô oæ .BYTÅ iî MOÓ Technologù syntax)® �
     Reservå bytå orienteä spacå anä itó contents¬ sucè aó �
     constants, variables or embedded text.
     Examples:
          db   0,0,0,0,22,105,0
          db   'text',0
     Iæ anù valuå evaluateó tï greateò thaî 0FFh¬ aî erroò wilì �
     be generated.
DW   definå worä (equivalenô oæ .WORÄ iî MOÓ Technologù syntax)® �
     Reservå word-orienteä spacå anä itó contents¬ witè thå �
     contentó storeä iî lo-hé order» typicallù useä tï definå �
     address tables.
     Example:
          dw   word1,word2,0,0FFFFh
DS   definå reserveä areá witè undefineä contents» typicallù useä �
     to define scratchpad areas.
     Example:
          ds   255

Defining constants or variables
-------------------------------
EQU  assigî á constanô valuå tï 'label§ (equivalenô oæ '=§ iî MOÓ �
     Technologù syntax)® Thå labeì musô bå iî thå samå line® �
     Valueó arå considereä tï bå 16-biô unsigneä numbers¬ anä maù �
     bå addresses¬ characteò constants¬ oò 16- oò 8-biô valueó oæ �
     anù kind® Iæ á constanô ió defineä morå thaî oncå usinç EQU¬ �
     aî erroò wilì bå generated.
     Example:
          eof  EQU  1ah
SET  assigî á variablå valuå tï 'label'® Thå samå aó EQU¬ excepô �
     thaô nï erroò wilì bå generateä iæ iô ió redefined® �
     Typicallù useä tï specifù variableó tï controì oò foò uså iî �
     conditional assembly.
     Example:
          flag SET 1
ŠDefining the location counter
-----------------------------
ORG  Defineó thå currenô locatioî counteò froí whicè addresseó �
     wilì bå calculateä (samå aó '*=§ iî MOÓ Technologù syntax)® �
     Maù bå defineä oò redefineä aô anù timå -- shoulä onlù bå �
     defineä tï á higheò address¬ aó redefinitionó tï loweò �
     addresseó thaî thå currenô addresó maù causå problemó aô �
     finaì assembly.
     Example:
          org 0f000h
END  Defineó thå enä oæ thå prograí aó faò aó assemblù ió �
     concerned. Optional.

Conditional assembly
--------------------
IF   Starô oæ sectioî whicè wilì bå assembleä onlù iæ thå �
     followinç conditioî ió truå (non-zero)® Onlù onå leveì oæ �
     conditional assembly is available.
     Example:
          testversion    equ  1
          IF testversion
                         jsr  printstatus
          ENDIF
          IF not testversion
                         jsr clrstatus
          ENDIF
                         jmp mainloop
ENDIF
     Endó á sectioî oæ conditionaì assembly® Á missinç oò �
     unmatched ENDIF will cause an error to be generated.

Unimplemented instructions
--------------------------
Thå followinç instructionó arå treateä aó reserveä words¬ buô �
arå noô yeô implementeä -- theiò uså wilì causå aî erroò tï bå �
generated:
     MACRO
     ENDM
     TITLE

Error messages
--------------
Assemblù erroò messageó arå rudimentary¬ consistinç oæ á singlå �
letteò iî thå firsô columî oæ thå listinç (.PRN© filå anä thå �
displaù oî thå consolå oæ thå relevanô line® Wherå severaì erroró �
occuò withiî thå samå line¬ onlù thå letteò oæ thå firsô erroò �
wilì bå shown® Iî general¬ thå causå oæ aî erroò wilì bå aó �
describeä iî thå lisô iî thå ASÍ manual» aî exceptioî ió thaô alì �
illegaì addressinç modeó arå treateä aó 'R§ (register© errors¬ �
foò whicè threå NOPó ('EAEAEA'© wilì bå generateä aó code®

Aó witè ASM¬ assemblù continueó afteò alì errors¬ sometimeó �
causinç otheò erroró lateò durinç assemblù aó á 'knock-on§ �
effect.



ŠUsing ASM65
-----------
Wå assumå thaô yoõ havå createä youò prograí oî á sourcå filå �
calleä 'filename.A65'® (Notå thaô thå filå musô uså thå extensioî �
'.A65')® ASM6µ caî creatå uð tï twï additionaì fileó froí thå �
sourcå fileº á '.HEX§ file¬ containinç machinå codå iî Inteì heø �
format¬ and/oò á '.PRN§ listinç file» iô caî alsï lisô tï thå �
console® Iî alì caseó sourcå lineó witè erroró wilì bå listeä tï �
thå screeî and¬ iæ thå printeò ió enabled¬ tï thå printeò aó �
well.

Typical examples of assemblies are:

     B>a:asm65 filename

whicè assumeó á sourcå filå filename.A6µ oî thå Bº drive¬ anä �
creates files filename.HEX and filename.PRN on the same drive.

     B>a:asm65 filename.bbz

which does the same, except that no .PRN file will be created.

     B>a:asm65 filename.bzx

whicè readó thå sourcå filå oî B:¬ doeó noô creatå á .HEØ file¬ �
anä sendó thå listinç onlù tï thå screeî withouô creatinç á .PRÎ �
file.

Notå thaô á .PRÎ filå maù welì bå twicå thå sizå oæ youò originaì �
sourcå fileº makå surå thaô yoõ havå enougè disë spacå beforå �
allowing the assembler to create it!

Foò fulì detailó oî thå actuaì assemblù procesó anä itó erroò �
messages, refer to the ASM manual.


Creating executable code
------------------------
ASM6µ doeó noô bù itselæ creatå executablå codå -- iô createó á �
'.HEX§ filå containinç itó machinå codå aó loaä address¬ heø �
valueó anä checksuí iî thå Inteì heø format® Thió musô bå �
converted to executable code by a separate loader.

Digitaì Research'ó LOAÄ prograí doeó thió foò 8080/Z8° programs¬ �
anä wilì alsï bå suitablå foò non-ROMablå 650² code® Thå catcè �
witè LOAÄ ió thaô iô alwayó createó á filå assuminç á loaä �
addresó oæ 100h¬ whereaó ROMablå 650² codå wilì tenä tï residå �
mucè higheò iî memory» LOAÄ thereforå tendó tï creatå aî oversizå �
filå consistinç mainlù oæ garbage¬ witè thå actuaì codå uð aô thå top® �
Thå solutioî iî theså caseó ió tï pasó thå heø filå tï aî externaì 650² �
systeí foò processinç it¬ oò uså thå  modifieä loader¬ CODE.COÍ (oî �
thió disk)¬ whicè automaticallù generateó aî offseô tï storå ROMablå �
codå iî thå minimuí sizå file® PROMLOAÄ oò somå otheò file-readeò caî �
theî transfeò thå codå tï aî externaì systeí oò PROÍ programmer.