SCAN USER'S MANUAL
                     SCAN USER'S MANUAL







                        Reed Powell
                  Digital Equipment Corp.
          Western Region Software Operations Group
                  Santa Clara, California

                         11-June-79



                       EDITION:  2.5
                       EDITION:  2.5
-OLS






          This manual reflects the status of SCAN,
          Version  7(11,541)  This  is  a modified
          version of SCAN 7(541), which contains a
          number  of  additions,  improvements and
          corrections   installed    at    On-Line
          Systems,   Inc.    ("OLS").    While  it
          reflects the overall  operation  of  any
          SCAN  release  from  7(541)  upwards, no
          guarantee   is   made    as    to    the
          applicability    or    correctness    of
          statements made herein.


          Ownership rights to the contents  remain
          Ownership rights to the contents  remain
          with  On-Line Systems, Inc., Pittsburgh,
          with  On-Line Systems, Inc., Pittsburgh,
          Pa.
          Pa.




                     Table of Contents
                     Table of Contents

 1.  Introduction

 2.  Routine Call Definitions

 3.  The Command Scanners (Overview)

 4.  Defining Switches - "SWTCHS" Macro

 5.  The "DM" and "KEYS" Macros

 6.  Defining the "STORAGE" Field

 7.  Default Value Handling

 8.  File-Spec Scanning

 9.  ISCAN - Scanner Initialization

10.  TSCAN - The Traditional Scanner

11.  OSCAN - Options File Scanning

12.  VSCAN - The Verb Form Scanner

13.  PSCAN - The Partial Mode Scanner

14.  Accessing SCAN

15.  Example of Using SCAN

16.  Using the Miscellaneous Routines

17.  Appendices:

      o  Notes on using SCAN
      o  Notes on using WILD
      o  DEC/OLS differences in SCAN and WILD
      o  SCNMAC
      o  $SCNDC
      o  SWTCHS, DOSCAN, DM & KEYS Examples
      o  LIST OF CUSPS & THE SCANNERS THEY USE



18.  Index














                         CHAPTER 1

                        INTRODUCTION













 1.1  INTRODUCTION

      SCAN is a  library  of  well-written  routines  of  general
 applicability  to  a wide variety of user programs.  Included in
 SCAN are:  command scanners;  input and output routines for file
 specifications,  numbers,  dates, strings and characters;  space
 allocation;  data management;  universal date-time  conversions;
 register  saving;  and indirect-file handling.  All routines are
 written to  be  virtually  independent  of  the  main  program's
 register conventions.  Only two constraints exist:

    o  AC17 must be a stack pointer, with a stack depth  at  call
       time of at least 15.

    o  AC1  and  AC7  are  used  to  pass  arguments,  and  (when
       applicable), return values.


 All routines will preserve  any  registers  which  they  do  not
 return a value in.

      The default  character  input  and  output  method  is  via
 TTCALLs,  but the user is free to specify the address of his own
 routine if he so desires.  For character input,  the  same  rule
 applies, but the user must always call an initialization routine
 as well.  The routines described in chapter two  will  be  those
 which are the most generally useful, and fall into the following
 groupings:

INTRODUCTION                                             Page 1-2


        Initialization
        Register Saving
        Space Allocation
        Output Routines - all
        Input Routines - numbers, dates, file-specs, and words



 The register mnemonics used will be those of SCAN, which are:


 T1 - T4:  1-4 ("Temporaries")
 P1 - P4:  5-10 ("Permanents")
       P:  17 ("Stack Pointer")



      All calls are via a PUSHJ, and  return  at  the  call+1  or
 call+2.  SCAN is loaded in library search mode from (70001,1).

      (See the section on "Accessing SCAN and its Macros".)













                            CHAPTER 2

                    ROUTINE CALL DEFINITIONS




2.1  INITIALIZATION


       .TYOCH - Use the address in T1  as  the  typeout  routine.
               Returns the previous routine's address (if any) in
               T1.

       .ISCAN - Initialize for input.  T1  is  a  pointer  to  an
               argument block:

               T1/ LENGTH,, BLOCK

               BLOCK:  Z
               +1:  Z
               +2:  INPUT ROUTINE,,OUTPUT ROUTINE
               +3:  Z
               +4:  Z
               +5:  Z

               If "Input Routine" or "Output Routine"  (or  both)
               is zero, then TTCALL I/O (e.g.:  INCHWL or OUTCHR)
               is used.  The chapter on  ".ISCAN"  describes  the
               meanings  and  usages  of  the  other words in the
               argument blocks.




               -----------------------------------------------

NOTE:  Those routine descriptions marked with an asterisk (*)  in
          the  outer  left  hand  margin  are  not  a part of the
          standard Digital supplied  SCAN.   These  routines  are
          peculiar to the modified version of SCAN for which this
          manual was written.

ROUTINE CALL DEFINITIONS                                 Page 2-2
REGISTER-SAVING                                         11 Jun 79


 2.2  REGISTER-SAVING


       .SAVE1 - Save P1
       .SAVE2 - Save P1-P2
       .SAVE3 - Save P1-P3
       .SAVE4 - Save P1-P4
       *.SAV1T - Save T4
       *
       *.SAV2T - Save T3-T4
       *
       *.SAV3T - Save T2-T4
       *
       *.SAVET - Save T1-T4
       *
       .POPJ  - Non-skip return (do a POPJ)
       .POPJ1 - Skip return
       .PSH4T - Stack T1-T4
       .POP4T - Unstack T1-T4

 All of the .SAVxx routines automatically restore  the  registers
 on  a  skip or non-skip return from the routine which called the
 .SAVxx routine.







 2.3  SPACE

 ALLOCATION

      *.GTWDS - Allocate (upwards from .JBFF) the number of words
      *
               in  T1.   T1  is returned with the address, if the
               allocation was successful, of the first word.  The
               allocated  area  will be zeroed.  On a failure, T1
               will  contain  the  negative   number   of   words
               available.





 2.4  OUTPUT ROUTINES - TEXT


       .TSIXN - Type T1 in SIXBIT.
       .TSTRG - Type ASCIZ string which T1 points to.
       .TXWWW - Type a wild octal word;  T1 contains the word, T2
               contains the mask.
       .TMOHW - Type a wild octal half word;  the word is  in  LH
               of T1, the mask is in RH.



ROUTINE CALL DEFINITIONS                                 Page 2-3
OUTPUT ROUTINES - DATE/TIME                             11 Jun 79


 2.5  OUTPUT ROUTINES - DATE/TIME


       .TDTTM - Type the date and  time  which  is  in  T1;   the
               argument is in the Universal Date/Time format.
       .TDATE - Type the date which is in T1;  the argument is in
               the standard DEC format (a la DATE UUO).
       .TDATN - Type the current date.
       .TTIME - Type the time which is in T1;   the  argument  is
               the  number  of  milliseconds  past midnight (a la
               MSTIME UUO).
       .TTIMN - Type the current time.





 2.6  OUTPUT ROUTINES - NUMBERS


       .TDECW - Type T1 as a decimal number.
       .TDEC2 - Type T1 as a decimal number  with  at  least  two
               positions;  fill character is in T2.
       .TOCTW - Type T1 as an octal number.
       .TRDXW - Type T1 in the radix which is in T3.
       .TXWDW - Type  T1  as  an  octal  number,  in  XWD  format
               (LH,,RH)
       .TVERW - Type T1 as a standard DEC version number.
       .TCORW - Type T1 as a core size, in P, K, or Words.
       .TBLOK - Type T1 as a file size, in Blocks or Words.
       .TPPNW - Type T1 as a PPN.





 2.7  OUTPUT ROUTINES - FILE SPECIFICATIONS


       .TOLEB - Type a file-spec.   T1  points  to  an  OPEN  UUO
               block;   T2  points to an extended LOOKUP or ENTER
               UUO block of at least four words.



ROUTINE CALL DEFINITIONS                                 Page 2-4
OUTPUT ROUTINES - CHARACTER                             11 Jun 79


 2.8  OUTPUT ROUTINES - CHARACTER


       .TCHAR - Type T1 as an ASCII character.
       .TFCHR - Type T2, using mnemonics  and  abbreviations  for
               non-printing characters, and preceeding lower-case
               characters with an apostrophe.
       .TCRLF -
       .TSPAC -
       .TTABC - Type a horizonal tab.
       .TCOLN - Type a colon.
       .TASTR - Type an asterisk.
       .TRBRK - Type a right bracket character.
       .TCOMA - Type a comma.
      *.T2CRL -
      *
      *.T4CRL - Type 1, 2 or 4 CRLF's, respectively
      *
      *.T2SPC -
      *
      *.T4SPC - Type 1, 2, or 4 spaces, respectively
      *
      *.TPLUS - Type a plus sign.
      *
      *.TSLSH - Type a slash character.
      *
      *.TAPOS - Type an apostrophe.
      *
      *.TCART - Type a caret (up arrow on some printers).
      *
      *.TRPAR - Type a right parenthesis.
      *
      *.TRANG - Type a right angle bracket
      *
      *.TLPAR - Type a left parenthesis.
      *
      *.TLBRK - Type a left bracket.
      *
      *.TLANG - Type a left angle bracket.
      *
      *.TAMPR - Type an ampersand.
      *
      *.TAROW - Type a left arrow (underscore on some printers).
      *
      *.TATSI - Type an at-cost sign.
      *
      *.TDASH - Type a dash.
      *
      *.TDOLR - Type a dollar sign.
      *
      *.TEQUL - Type an equal sign.
      *
      *.TEXCL - Type an exclamation mark.
      *
      *.TPCNT - Type a per cent sign.
      *
      *.TSEMI - Type a semi-colon.
      *
      *.TQUOT - Type a double-quote mark.
      *
      *.THASH - Type a hash mark ("#").
      *
      *.TBKSL - Type a back-slash character ("\").
      *

ROUTINE CALL DEFINITIONS                                 Page 2-5
INPUT ROUTINES - INTRODUCTION                           11 Jun 79


 2.9  INPUT ROUTINES - INTRODUCTION

      The input routines will  normally  leave  their  result  in
 accumulator  "P3"  - which they use under the alias "N".  Single
 character input routines will use "P4", under the alias "C".

      Most routine descriptions given below will list two  names;
 the  second one will often be the same as the first but with the
 last character of the name changed to "C".  The  second  routine
 entry  point is used when the next character in the input stream
 is already in accumulator "CH" ("P4"), while the  first  routine
 entry  point  is  used when the next character in the stream has
 not yet been input.

      This ability to  already  have  the  next  input  character
 waiting  is  used  in  conjunction  with  the so called "re-eat"
 facility of SCAN, which  allows  a  program  to  look-ahead  one
 character.  The routine ".REEAT" is used to perform this, and is
 described later in this chapter in  the  section  "MISCELLANEOUS
 ROUTINES."

      More information on this is  included  in  the  chapter  on
 USING THE MISCELLANEOUS ROUTINES.

ROUTINE CALL DEFINITIONS                                 Page 2-6
INPUT ROUTINES - STRING AND NUMERIC                     11 Jun 79


 2.10  INPUT ROUTINES - STRING AND NUMERIC


       .SIXSW, .SIXSC - Input a SIXBIT word into P3.
       .OCTNW, .OCTNC - Input an octal number into P3.
       .DECNW, .DECNC - Input a decimal number into P3.

                       Optional suffixes for  decimal  and  octal
                       input  are:   K,  M  and  G,  for the base
                       raised to the  third,  sixth,  and  nineth
                       power, respectively.

       .NAMEW, .NAMEC - Input a possibly wild SIXBIT word;   word
                       is in P3, mask is in "MASK".

       .ASCQW, .ASCQC - Input a  possibly  quoted  ASCII  string.
                       The  string  will  be  input into the area
                       (inside  SCAN)  beginning  at  the  global
                       symbol  ".NMUL",  and extending no further
                       than the symbol ".NMUE".  Input terminates
                       at  the  first non-alphanumeric character.
                       Any characters  within  the  string  being
                       typed,  but  which  cannot be fit into the
                       buffer, is lost.  Since  the  symbols  are
                       global,   they  are  accessable  from  the
                       calling program, which should BLT them  to
                       a safe place.

       .SIXQW,  .SIXQC  -  This   functions   exactly   as   does
                       .ASCQW/.ASCQC   above,   except  that  the
                       characters are  stored  in  SIXBIT  rather
                       than ASCII.

       .SIXMW,  .SIXMC  -  This   functions   exactly   as   does
                       .SIXQW/.SIXQC above, except that the input
                       string cannot be quoted.






 2.11  INPUT ROUTINES - DATE/TIME



                       [More  information  on  this  subject   is
                       contained  in  the  later chapter on USING
                       THE MISCELLANEOUS ROUTINES]

       .DATIM, .DATIC - Input date-time into P3,  storing  it  in
                       universal format.
       .DATIP, .DATIQ - Input a date-time in the  past  into  P3,
                       storing it in universal format.

ROUTINE CALL DEFINITIONS                                 Page 2-7
INPUT ROUTINES - DATE/TIME                              11 Jun 79


       .DATIF, .DATIG - Input a date-time in the future into  P3,
                       storing it in universal format.

      Legal date-time formats, examples and explanations are:

ROUTINE CALL DEFINITIONS                                 Page 2-8
INPUT ROUTINES - DATE/TIME                              11 Jun 79


                        FORMAT          EXAMPLE         EXPLANATION

                       DATE-SPEC:
                        day             WED             WEDNESDAY
                        day offset      123D            123 days
                                                        ago from now
                        MM-DD           6-12            Jun. 12
                        MM-DD-Y         6-12-6          Jun. 12, 1976
                        MMM-DD-YY       JUN-12-76       June 12, 1976
                        DD-MMM-YYYY     12-JUN-1976     June 12, 1976
                        Mnemonic        YESTERDAY
                                        TOMORROW
                                        TODAY

                       TIME-SPEC:
                        HH              12              noon
                        HH:MM           13:02           2 past 1 PM
                        HH:MM:SS        1:02:37         37 secs past
                                                        1:02 AM
                        mnemonic        NOON
                                        LOGIN


                       DATE-TIME:
                        date-spec:time-spec     JUN-12-76:13:02:37




 2.12  INPUT ROUTINES - VERSION NUMBER



       .VERSW, .VERSC - Input a version number into P3.   Version
                       number format is:


                       NNMM(EE) where:

                            NN is the major version, blank to 511
                            MM is the minor version, blank to ZZ
                            (EE) is the edit number,
                              blank to 202,143




ROUTINE CALL DEFINITIONS                                 Page 2-9
INPUT ROUTINES - CORE & FILE SIZES                      11 Jun 79


 2.13  INPUT ROUTINES - CORE & FILE SIZES



       .COREW, .COREC - Input a core size in words, pages, or  K;
                       suffixes  are:   W  (default),  P  and  K,
                       respectively.  Returns size, in words,  in
                       P3.
       .BLOKW, .BLOKC - Input a file size  in  words  or  blocks;
                       suffixes  are:  W (default) or B.  Returns
                       size in words in P3.






 2.14  INPUT ROUTINES - CHARACTERS



       .TICAN -  Check  for  an  alphanumeric  character  in  P4.
               Non-skips if not alphanumeric, skips if it is.
       .TIMUC - Convert character in P4 to upper case, if  it  is
               in lower case.
       .TIAUC - Input a character into P4, handling  lower  case,
               altmodes and all compressions.
       .TIALT - Input a character, handling  altmodes  and  space
               compression, into P4.
       .TIGET - Gets a character into P4, with no equivalencing.


               For .TIAUC and  .TIALT,  P4  is  returned  in  the
               following format:

               1-177:   actual character
                   0:   end-of-line character
                  -1:   altmode
                  -2:   end-of-file
                       (Control Z or EOF on indirect file)

                The   following   are   Guide    Words    (pseudo
               characters):

                4000:   'AND'
                4001:   'OR'
                4002:   'NOT'
                4003:   'TO'
                4004:   'FROM'
                4005:   'INPUT'
                4006:   'OUTPUT'
                4007:   'SOURCE'
                4010:   'LIST'
                4011:   'OBJECT'

ROUTINE CALL DEFINITIONS                                Page 2-10
Input:  Character, File Specifications                  11 Jun 79


                    See "SYNTAX REPRESENTATIONS"  in  Chapter  8.
               Also refer to Appendix D - "SCNMAC."






 2.15  INPUT ROUTINE - FILE SPECIFICATIONS



       .FILIN - Input a file specification.  Details on its usage
               is   the  subject  of  a  later  chapter  in  this
               document.

ROUTINE CALL DEFINITIONS                                Page 2-11
MISCELLANEOUS ROUTINES                                  11 Jun 79


 2.16  MISCELLANEOUS ROUTINES


       .RUNCM - Process a /RUN specification,  if  any  has  been
               encountered.   No arguments are possible;  returns
               only if no /RUN was ever seen on the line,  or  if
               the  RUN  UUO failed.  Usually called right before
               normal program termination  code.   More  on  this
               routine  in  included  in a later chapter on USING
               THE MISCELLANEOUS ROUTINES.


       .MKPJN - Make a CCL job number.  Call with the job  number
               (or  whatever) in T1.  Returns with SIXBIT form of
               argument in (RH) of T1.  More information is in  a
               later chapter on USING THE MISCELLANEOUS ROUTINES.


       .LKNAM - Do a table search for  an  exact  or  abbreviated
               match.   Call  with  SIXBIT  value  in  T2,  and a
               pointer in T1 of the form:

                   IOWD length, table-address


                    Skip-returns if a match was found, with  (RH)
               of  T1  pointing to the match, and (LH) of T1 zero
               if it was abbreviated, or  negative  if  an  exact
               match.   Non-skip returns if unsuccessful, with T1
               negative if no match was  found,  or  positive  if
               multiple  matches  were  found.   A  later chapter
               (USING THE  MISCELLANEOUS  ROUTINES)  covers  this
               routine in greater detail.


      *.RAND - Generate a random number between  0  and  2**18-1,
      *                                                   **
               storing it in T1.
      *.RANDM - Same as .RAND, but on call T1 contains the  upper
      *
               bound    on    the   result.    Method   used   is
               "middle-squares."


               [More information on the  following  routines  for
               date  and  time  conversion is included in a later
               chapter:  USING THE MISCELLANEOUS ROUTINES]

       .CNTDT - Convert  universal  date/times  to  DEC  formats.
               Call  with  universal form in T1, returns with DEC
               date in T2, and MS in T1.
       .GTNOW - Get current date and time, in  universal  format,
               into T1.
       .CNVDT - Convert DEC format date/time to universal format.
               Call  with  time  in  T1,  stored as the number of
               milliseconds past midnight (MSTIME UUO).  The date

ROUTINE CALL DEFINITIONS                                Page 2-12
MISCELLANEOUS ROUTINES                                  11 Jun 79


               is  in T2, stored in the standard DEC format (DATE
               UUO).  Returns universal form in T1 (or -1 if date
               was beyond September 27, 2217).  Note that "Day 0"
               was a Wednesday, and so (T1)/7 gives a day of week
               index, with Wednesday being 0.



ROUTINE CALL DEFINITIONS                                Page 2-13
MISC:  Scan-Block Conversion, Input Back-Spacing        11 Jun 79


       .STOPB - Convert a "scan-block" (see the later section  on
               "FILE-SPEC   SCANNING")   to   OPEN  and  extended
               LOOKUP/ENTER blocks.  Call with:

                  T1/ length,,address of scan-block
                  T2/       ,,address of OPEN block
                  T3/ length,,address of LOOKUP block
                  T4/       ,,address of PATH block (9 words)

               Returns non-skip (error) if  any  wild-cards  were
               seen    in    the    scan-block;    otherwise   it
               skip-returns.


       .REEAT - Cause the contents of P4 to be the next character
               to  be read.  P4 will normally contain the current
               character.  Call is simply

                  MOVEI P4, char
                  PUSHT P,.REEAT  

               More information on this routine, and the  general
               concept  of  positioning  input  from  the command
               line, is covered in a later chapter on  USING  THE
               MISCELLANEOUS ROUTINES.


       .CLRBF - This routine will clear any  type  ahead  in  the
               input  stream.  No arguments are passed, no values
               returned, and control always comes to the  calling
               point +1.

       .GTWRD - Get a word from a list.  Call with:

                    T1/ table address
                    T2/ length of table

               On return (always to Call +1), the values are:

                    T1/ incremented by 1
                    T2/ decremented by 1
                    T3/ data from list, or 0 if at end

               This routine is covered in greater  detail,  along
               with  the  following  routine (.PTWRD), in a later
               chapter on USING THE MISCELLANEOUS ROUTINES.
       .PTWRD - Put a word into a list.  This is meant to be used
               along  with .GTWRD, above.  Control always returns
               to the call +1 location.  Calling sequence is:

ROUTINE CALL DEFINITIONS                                Page 2-14
MISC:  Scan-Block Conversion, Input Back-Spacing        11 Jun 79


                    T1/ table address
                    T2/ maximum table length
                    T3/ data to be stored
                    PUSHJ P,.PTWRD##
                    T1/ incremented by 1
                    T2/ decremented by 1
                    T3/ old data from location stored into


       .MKMSK - This routine makes a mask for its argument  word.
               The  argument  must  be  SIXBIT  data.   The  mask
               contains 1s where  the  argument  had  non-blanks.
               Calling sequence is:

                    MOVE T3,argument
                    PUSHJ P,.MKMSK  -always returns here-
                    T1/ mask for argument

               More information on this routine is in the chapter
               USING THE MISCELLANEOUS ROUTINES.


       .TDIRB - This  routine  is  used  to  type  out  directory
               blocks.   Three formats are accepted:  1) Extended
               LOOKUP/ENTER blocks;   2)  PATH  blocks;   and  3)
               "bi-words", which is an internal SCAN format.  The
               calling sequence is:

                    HRLI T1,code
                    HRRI T1,address
                    PUSHJ P,.TDIRB##
                     -always returns here-

                    where "code" is one of the following:

                    1 if (RH) is address of LOOKUP/ENTER block
                    2 if (RH) is a PATH block address
                    3 if (RH) is address of "bi-words"

               More information on .TDIRB is in the chapter USING
               THE MISCELLANEOUS ROUTINES.


       .ISLGI - This routine is used to test to determine if  the
               calling  job is logged in.  No argument is passed.
               The value returned is:

                    PUSHJ P,.ISLGI##
                     -here with T1=-1 if not logged in, or
                                T1=1 if indeterminate
                     -here if logged in (skip ret)













                            CHAPTER 3

                      THE COMMAND SCANNERS



 3.1  INTRODUCTION

      This chapter will discuss the  types  of  command  scanners
 provided  by  SCAN.   The  actual  details  of usage are covered
 separately in later chapters on each scanner.   The  purpose  of
 this  chapter is to present the concepts of command scanners and
 switch types which are relevant to determining which scanner  is
 best for various applications.



 3.2  OVERVIEW OF THE 4 SCANNERS

      Within SCAN there are four basic Command Scanning routines,
 and an initialization routine.  The four scanners all accept the
 same  switch  formats;   their  only  differences  lie  in   the
 structure of the command line itself.  The scanners are:




 3.2.1  TSCAN

      This is the so-called "Traditional Scanner." Command  lines
 are of the form:

                      OUTPUT = INPUT
                      OUTPUT = INPUT,INPUT, ...
                           or
                      INPUT

 Users of this syntax are PIP and DIRECT.


THE COMMAND SCANNERS                                     Page 3-2
OVERVIEW OF THE 4 SCANNERS                              11 Jun 79


 3.2.2  VSCAN

      This is the "Verb Form Scanner." Command lines look like:

                      COMMAND-WORD /SWITCH/SWITCH
                      COMMAND-WORD /SWITCH/SWITCH FILE-SPEC
                           or
                      COMMAND-WORD

 DUMP and BACKUP programs are users of this format.




 3.2.3  OSCAN

      This  is  the  "Option  File  Scanner."  This   scans   the
 options-file SWITCH.INI for entries of the form:

                      NAME /SWITCH/SWITCH
                           or
                      NAME:OPTION /SWITCH/SWITCH


 Users of this feature include LOGIN, DIRECT,  BACKUP,  SOS,  and
 ALKFIL.




 3.2.4  PSCAN

      PSCAN is the "Partial Mode" Scanner.  Commands are  of  the
 TSCAN  style,  but  only  part of the line is processed by SCAN.
 Command lines might be of the format:

                      mumble mumble /SWITCH /SWITCH

 In this case, the "mumble mumble" portion of the  command  could
 be parsed by the user program, and PSCAN would be used to do the
 "/SWITCH" processing.  An example of a PSCAN user is CREDIR.



THE COMMAND SCANNERS                                     Page 3-3
SWITCH-FORMATS:                                         11 Jun 79


 3.3  SWITCH-FORMATS:



      The general formats of a  switch  specification  are  quite
 simple  -- which format a particular switch will require depends
 on how it is defined in the SWTCHS Macro (described later).

      The simplest switches are those which take no value  --  it
 is their presence (or absence) which is important.  The presence
 of the switch will cause SCAN to deposit a predefined value into
 a predefined memory byte or word.  It is also possible for these
 switches to  be,  in  effect,  three-way  rather  than  two-way.
 Either  the  switch  is  absent,  present,  or present with "NO"
 prefixed to it.  Examples of these types of switches are:

      /FAST
      /HELP
      /MAP
      /NOMAP



      The second type of switch is one that  takes  a  value  (or
 values) which must be part of a pre-defined list of legal values
 for that switch.  The "value" of the switch is then the  numeric
 index,  into  the table of legal values, of the value specified.
 For example, if the legal values for "/MODE" were "ASCII, OCTAL,
 SIXBIT, DECIMAL," then:

      /MODE:OCTAL       value = 1
      /MODE:DECIMAL     value = 3
      /MODE             is illegal


      A variation of this switch allows for defaults when:

    o  The switch was not mentioned.
    or
    o  The switch was mentioned, but without an explicit value.



      The third type of switch is one that takes a more  or  less
 arbitrary  value.   This value can be anything the user desires.
 SCAN is supplied with the name of a  routine  to  "pick-up"  the
 value,  and  a  description of where and how to store the value.
 If desired, a maximum value may be specified.  In addition,  the
 comment  above  about  defaults  for  Type 2 switches also holds
 here.  The switch may be defined to take only one value,  or  to
 take   many   values.   Typical  values  are  numbers  and  file
 specifications.  Examples are:

THE COMMAND SCANNERS                                     Page 3-4
Switch Formats                                          11 Jun 79


      /WIDTH:75
      /ABCD:(12,34,56,78)
      /FILE:MYFIL.MAC[70001,1]

 The three basic switch types can be summarized as:

      TYPE 1 - no value
      TYPE 2 - specific values only
      TYPE 3 - arbitrary values







 3.4  FILE-SPECIFICATIONS


      The format of  a  file  specification  for  SCAN  is  quite
 general.   No ordering between the components is either expected
 or necessary.  The basic parts of a file-spec are:


  o  DEVICE:  1-3 SIXBIT characters followed by a colon.

  o  FILENAME:  1-6 SIXBIT characters.

  o  EXTENSION:  1-3 SIXBIT characters, preceeded by a period.

  o  PPN:  A Project Number (1-377777 octal), a Programmer Number
     (1-377777  octal)  and (optionally) an SFD specification, in
     one of the following arrangements:

        [PROJECT,PROGRAMMER]
        [PROJECT,PROGRAMMER,sfd,sfd,...]
        [,PROGRAMMER]               uses logged-in PROJECT
        [,PROGRAMMER,sfd,sfd,...]         -dittoe-
        [PROJECT,]                  uses logged-in PROGRAMMER
        [PROJECT,,sfd,sfd,...]            -dittoe-
        [,]                         uses logged-in PPN
        [,,sfd,sfd,...]                  -dittoe-
        [-]                         uses default path

  o  SWITCHES:  Any of the switches described later as  "Internal
     Scan Switches." (See "FILE-SPEC SCANNING.")


THE COMMAND SCANNERS                                     Page 3-5
DEFAULT VALUES FOR SWITCHES                             11 Jun 79


 3.5  DEFAULT VALUES FOR SWITCHES

      When the user calls SCAN, he has the option of specifying a
 set  of defaults for any of the above components.  SCAN will use
 these defaults in the event that the user does not  specify  the
 corresponding  component  of  the  specification.   More of this
 topic is covered in detail in a later chapter -- "DEFAULT  VALUE
 HANDLING."













                            CHAPTER 4

             DEFINING SWITCHES - THE "SWTCHS" MACRO







4.1  DEFINING SWITCHES - "SWTCHS" MACRO

     The purpose of this chapter is to cover the topic of  switch
definition.  it is necessary for the user program to provide SCAN
with information on the switches to  be  parsed.   This  includes
data such as the switch name, the type of argument, if any, where
to store the parsed values, and the like.  The definition process
has been made relatively simple and painless by the use of macros
supplied by SCNMAC.



4.2  SWTCHS & DOSCAN -- USAGE

     The properties of each switch to be scanned for are  defined
via  a  set  of  MACROs  provided  by  SCAN.   There  is always a
one-to-one  correspondence  between  a  switch  and   its   MACRO
specification.   These  switch  MACROs  are all included within a
user defined MACRO called "SWTCHS".  The definition of SWTCHS  is
of the following simple form:



          DEFINE SWTCHS <
          macro-call .  .  .  .
          macro-call .  .  .  .
                 .
                 .
                 .
          macro-call .  .  .  .
          >;END OF SWTCHS MACRO



DEFINING SWITCHES - THE "SWTCHS" MACRO                   Page 4-2
SWTCHS & DOSCAN -- USAGE                                11 Jun 79


     Once the switches are defined in SWTCHS, the scanning tables
are  generated by calling the macro "DOSCAN".  The format of this
call is:

          DOSCAN (NAME)


where "NAME" is a legal MACRO-10 label from 1-5 characters.   The
tables  generated  for  use  by SCAN will have labels of the form
"NAMEx," where "x" identifies the  specific  table.   The  tables
involved are:



    o  nameN - The table of switch names  (in  SIXBIT),  one  per
       word.

    o  nameD - The table of default values.

    o  nameM - The table  of  routine  addresses  for  processing
       switch values.

    o  nameP - The table of pointers used for storing values.

    o  nameL - This symbol's value is the length of each  of  the
       above tables.




 4.3  SWTCHS -- DEFINITION

      There are four switch defining macros (USED WITHIN  SWTCHS)
 which    are   described   below:    SS   (Switch-Storage),   SN
                                      SS    S      S           SN
 (Switch-Name),  SL  (Switch-List),  and   SP   (Switch-Pointer).
  S      N       SL   S      L             SP    S      P
 fsyntax A "typical" switch-table definition might now look like:

      DEFINE SWTCHS <
      SS...
      SN...
      SL...
      SP...
      >
      DOSCAN (TEST)


 The switch macros and their parameters are:


   1.  SS - This is for switches described above as "TYPE 1".  No
       value  is  specified  on  the  command  line;   instead, a
       pre-defined value is stored.  The SS format is:


DEFINING SWITCHES - THE "SWTCHS" MACRO                   Page 4-3
SWTCHS -- DEFINITION                                    11 Jun 79


            SS NAME, STORAGE, VALUE, FLAGS

       When the switch is encountered, VALUE will  be  placed  in
       the    location   described   by   STORAGE.    FLAGS   are
       scan-controlling flags  which  will  be  described  later.
       STORAGE  may  be an address or a byte pointer.  Use of the
       POINTR macro for defining  the  STORAGE  field  latter  is
       described later.  An example of SS usage is:


            SS MAP,MAPLOC,1,0

       In this case, "1" is stored in MAPLOC if /MAP is  seen  on
       the command line.

   2.  SN - This is also for "TYPE  1"  switches,  in  the  cases
       where  "NO"  may  be  prefixed to a switch's defined name.
       The SN format is:


            SN NAME, STORAGE, FLAGS


            If the switch is encountered without the "NO" prefix,
       STORAGE  takes  the  value  "1."  If  the  prefix  "NO" is
       included, the value of STORAGE is then  "0."  STORAGE  and
       FLAGS are as defined for SS.  For example:

            SN INTERCHANGE,INTLOC,0

       If /INTERCHANGE were define in this manner, then  whenever
       /INTERCHANGE  appeared  on  the command line, "1" would be
       stored in INTLOC (as would be the case with SS).  However,
       if  /NOINTERCHANGE  were  seen  (which  would not be legal
       using SS unless a seperate SS definition were made),  then
       "0" would be put into INTLOC.

   3.  SL - This is used to define "TYPE 2" switches;  those with
       one  of  a  specific  set of values.  Associated with this
       macro are two others --  "KEYS"  and  "DM"  --  which  are
       called outside of SWTCHS.  The SL format is one of:
              _______

                 SL NAME,STORAGE,TABLE,DEFAULT,FLAGS
                 SL NAME,PROCESSOR,TABLE,DEFAULT,FLAGS



            STORAGE and FLAGS are as described  for  SS  formats.
       PROCESSOR   is  used  to  specify  a  non-standard  (i.e.:
       non-SIXBIT) input routine.   This  routine  is  then  also
       responsible  for  storing  the  value  as well.  TABLE and
       DEFAULT are names associated with the KEYS and DM  macros,
       respectively.

DEFINING SWITCHES - THE "SWTCHS" MACRO                   Page 4-4
SWTCHS -- DEFINITION                                    11 Jun 79


            The value placed in STORAGE will be  the  index  into
       the  table of values generated by KEYS.  The format of the
       MACRO-10 labels generated are  described  below  with  the
       KEYS macro.  An example of the SL format is:

                 SL PARITY,PARLOC,PARY,PAR,

       This will be explained once the KEYS  and  DM  macros  are
       described below.


   4.  SP - This format is used with "TYPE  3"  switches;   those
       which  take  an  arbitrary  value,  possibly  less  than a
       predefined maximum.  The SP format is:

                 SP NAME,STORAGE,PROCESSOR,DEFAULT,FLAGS

            STORAGE and FLAGS are  as  described  above  for  SS.
       PROCESSOR  is  the  address of the routine (either SCAN or
       User-supplied) to "pick-up" the value.  This routine  must
       leave  the  value in P3 if it wants SCAN to store it.  The
       routine must return +1 for SCAN to store the value, or  +2
       for  SCAN to not store the value.  DEFAULT is as described
       for SL and may be null if no defaults (or  maximum  value)
       are  desired.   Examples,  which will be explained in more
       detail later, are:

                 SP PROTECTION,PROTEC,.OCTNW##,,0
                 SP PROTECTION,PROTEC,.OCTNW##,PRO,0




      Each of these macros will uniquely identify and describe  a
 switch in terms of the following characteristics:

    o  Its name.
    o  Where to place its value, if any (STORAGE).
    o  How to read its value, if any (PROCESSOR).
    o  What its legal values, if any, are (TABLE).
    o  What its default and maximum values are, if any (DEFAULT).
    o  The syntax in which it may or may not be used (FLAGS).





 4.4  SCAN - CONTROLLING FLAGS:

      Each switch may have associated with it  a  combination  of
 any  of the following flags.  These flags control how the switch
 may be used in a command line.

DEFINING SWITCHES - THE "SWTCHS" MACRO                   Page 4-5
FS.??? Flags                                            11 Jun 79


    o  FS.VRQ - A value is required.

    o  FS.NFS - The switch is never part of a file-specification.
       This switch should be meant as a global switch.

    o  FS.LRG - The maximum and default values are 0  or  greater
       than  2**17.   If set, and the maximum value (in DM macro)
       is set, then 36-bit values for this switch  are  possible.
       Otherwise, only 18-bit values are legal.

    o  FS.NCM - This switch is not a command switch (for VSCAN).

    o  FS.NUE - No user exit on this  switch.   This  means  that
       /EXIT  and  ^Z  do  not  cause an exit via MONRET, as they
       normally would.

    o  FS.OBV - "OR bit values." This causes  the  value  of  the
       switch  to  be  OR-ed  with  whatever  existing  value may
       already have been stored.  Normally, the old value in  the
       STORAGE  location  is  overwritten.   If this flag is set,
       then SCAN will LDB the existing value, IOR in the value of
       the  switch as just parsed, and then DPB the value back to
       storage again.

    o  FS.NOS - For the SN macro calls  only:   This  switch  may
       take "NO" as a prefix.














                            CHAPTER 5

                    THE "DM" & "KEYS" MACROS







 5.1  THE "DM" AND "KEYS" MACROS

      These two scanning macros are those related to:  1) default
 (and  maximum) values, and 2) values for "TYPE 2" (SL) switches.
 These were mentioned above in the discussions of the SL  and  SP
 macros, and will now be described in detail.



 5.2  DM -- MAXIMUM & DEFAULT VALUES

      In order to supply SCAN with a set of default  and  maximum
 values,  the  programmer supplies a 1-3 character name in the SL
 or SP macro, in  the  field  DEFAULT.   After  SWTCHS  has  been
 defined, DM is called for each switch referencing it.  A DM call
 has the form:

           DM (NAME,MAX,ABSENT,PRESENT)

           where:

           NAME     is the 1-3 character name in  the  SL  or  SP
 PD.????
                    call.
           MAX      is the maximum value.
           ABSENT   is the default value if the switch is not
                    encountered.
           PRESENT  is the default value if the switch is
                    present, but without a value.

      Each of these values is given a symbolic name, if the  name
 already   is   defined,   then  the  existing  definition  takes
 precedence over the DM argument.  The three symbol names are  of
 the respective forms:

      MX.NAME AD.NAME PD.NAME

THE "DM" & "KEYS" MACROS                                 Page 5-2
"DM"                                                    11 Jun 79


 An example will clarify this somewhat.  Given the following:

      DEFINE SWTCHS <
      SP PROTECTION,PROTEC,.OCTNW##,PRO,0
      >
      DM (PRO,777,057,155)



      This defines a switch  "/PROTEC"  whose  maximum  value  is
 "777".   If  the  switch is not in the command line, THE PROGRAM
 (not SCAN) may use the symbol AD.PRO for the value, which may be
 "057."  If  only  "/PROTEC"  is  in the command string, then the
 value stored BY SCAN will be that of PD.PRO, in this case "155".



 5.3  KEYS - KEYWORD DEFINITION

      "TYPE  2"  (SL)  switches  always  take  a  value  from   a
 predefined  list  of keywords.  These keywords must be made from
 the SIXBIT characters, and are defined in the KEYS  macro.   The
 SL  macro's  TABLE  field  is  then used as an argument to KEYS.
 KEYS is called after SWTCHS is defined (just like DM  is).   The
 call is of the form:

           KEYS (NAME,WORD1,WORD2,...WORDn)

           where:

           NAME is the 1-4 character name from the SL call.
           WORD1 is the first possible value.
           WORD2 is the second possible value.
           WORDn is the last possible value.



      The table of values is given the  name  NAME.T  and  is  of
 length  NAME.L.   Each possible value's position in the table is
 the value of the symbol NAMExx, where "xx"  are  the  first  two
 characters  of  the  value.   This  implies  that  if these SCAN
 constructed symbols are  to  be  used  by  the  program  (not  a
 necessity),  then all keywords must be unique in their first two
 letters.

      Once  again,  an  example  is  in  order.    Consider   the
 following:

           DEFINE SWTCHS <
           SL PARITY,PARLOC,PARY,PAR
           >
           KEYS (PARY,EVEN,ODD,NONE)
           DM (PAR,PARY.L,PARYNO,PARYOD)

THE "DM" & "KEYS" MACROS                                 Page 5-3
"KEYS"                                                  11 Jun 79


      This generates a switch "PARITY" which takes as  a  "value"
 of of the following keywords:

           EVEN
           ODD
           NONE

 The default is "NONE" if only "/PARITY" is seen in  the  command
 without  an  explicit value.  If the "/PARITY" switch is missing
 from the command line altogether, then the  default  value  (not
 supplied  by SCAN) is "ODD".  The location "PARLOC" will receive
 the "value" of the switch, which is determined by the  order  in
 which the keywords are listed in the KEYS macro:

           EVEN=0
           ODD =1
           NONE=2


      The maximum value for such a switch is the VALUE  (not  the
 contents)   of  the  symbol  "PARY.L"  (ie,  the  1-4  character
 designater used in KEYS, with ".L" catenated to the right).

      The elemets of the DM call specifying the defaults  may  be
 the  symbolic  names constructed by the KEYS call, or the actual
 values (as literals or non-SCAN defined  symbols)  values.   The
 later  is normally undesireable, as it makes changing a switch's
 characteristics difficult, but is used when the possible  values
 (keywords)  cannot be unique in their first two letters.  If the
 non-unique values are not to also be default or maximum  values,
 then this poses no real problem (since the assembler will simply
 use the latest definition it encounters).



 5.4  CONSTRUCTED SYMBOLS - SUMMARY

      The previous sections has covered a number of symbols  used
 by SCAN and its support code that are created by the SCAN macros
 themselves.  To summarize them:

  o  MX.???  - ???  is first arg to DM;  this is created by DM as
     the maximum value for the switch
  o  AD.???  - as above, but this is the absent default value for
     the support program to use if it sees fit.
  o  PD.???  - as above, but this is the  present  default  value
     for the switch, used by SCAN.
  o  ????.L - ????  is the first agr to KEYS;  this is created by
     KEYS,  and  has  as  its  value  the  length of the table of
     keywords created by KEYS for this switch.
  o  ????.T - as above, but this is the address of the  table  of
     keywords created by KEYS.

THE "DM" & "KEYS" MACROS                                 Page 5-4
CONSTRUCTED SYMBOLS - SUMMARY                           11 Jun 79


  o  ????XX - as above, but this is the index into ????.T for the
     keyword whose first 2 characters are XX.
  o  ?????N - ?????  is the arg to DOSCAN (see previous chapter);
     this is the table of switch names.
  o  ?????D - as above, this is the table of default values
  o  ?????M - as above, this is the table of  processor  routines
     for the switch
  o  ?????P - as above, this is  the  table  of  information  for
     storing values.
  o  ?????L - as above, this is the length of  the  other  tables
     created by DOSCAN.














                            CHAPTER 6

                  DEFINING THE "STORAGE" FIELD







6.1  DEFINING THE "STORAGE" FIELD

     All  of  the  Switch   macros   have   the   field   denoted
"STORAGE."  This  field  can  have a number of formats, sometimes
depending on the switch macro itself.  Each of the  formats  will
be described here.



6.2  THE POINTR MACRO

     One of the principle uses of STORAGE is as a  byte  pointer.
Because  of  this,  it  is useful to first mention the use of the
POINTR macro, since it is quite often the method used  to  define
the STORAGE field.

     This macro is used to define a byte pointer, given:  1)  the
definition  of  the  byte  in terms of a mask, and 2) the storage
location containing the byte.   An  example  might  prove  useful
here.  Suppose a word "Y" contains a byte "X," consisting of bits
11 through 19.  The POINTR usage would then be:

      X=177600000;  mask for bits 11-19
      POINTR (Y,X)      


 If "X" were changed to be some other byte, either in "Y"  or  in
 some  other  location,  the  only  change needed would be to its
 definition;  references to it via the  POINTR  macro  would  not
 need changing

DEFINING THE "STORAGE" FIELD                             Page 6-2
STORAGE FIELD                                           11 Jun 79


 6.3  STORAGE FIELD

      There are five formats for STORAGE:
 1.  Word Address.  (SN,SS,SP,SL)
 2.  Byte Address.  (SN,SS,SP,SL)
 3.  Pointer to multiple-value storage.  (SS,SP,SL)
 4.  Pointer to a file-specification storage area.  (SP)
 5.  Address of a routine to process keyword.  (SS,SP,SL)


      For all formats except #1, STORAGE is in the  format  of  a
 PDP-10 byte pointer, although it may not always be used as such.
 The exact format definitions for the five types, in order are:

  1.  (LH)=0
      (RH)=word address;   value  is  MOVEMed  into  the  storage
      address.

  2.  Standard byte pointer format;   value  is  DPBed  into  the
      storage field.

  3.  The byte size field contains the number  of  words  in  the
      storage  area, in the form (65-#words).  (RH) points to the
      first word.

  4.  This is implicit:  ".FILIN" will have  been  given  as  the
      PROCESSOR.   (RH)  is  the address of the SCAN storage area
      (see later discussion of SCAN blocks).  The length of  this
      area  (see later discussion of SCAN blocks) is the value of
      MX.NAME (from the DM call), which would otherwise  have  no
      meaning in this context.

  5.  Bits 0 through 11 in the "byte-pointer" being all 1s  means
      that (RH) is the dispatch address of a processor which will
      "pick-up" the keyword.e a dummy symbol to be  the  required
      value,  The  easiest  method  of  specifying  such  a value
      (getting both the size and position fields to be 1s) is  to
      deine  a dummy symbol to be the required value, and to then
      use that symbol in the STORAGE field.














                            CHAPTER 7

                     DEFAULT VALUE HANDLING



7.1  INTRODUCTION

     In Chapter five ("THE 'DM' AND 'KEYS' MACROS"), the  concept
of  specifying  default  values  for  the  various  switches  was
introduced.  This chapter will cover the topic  in  more  detail.
Both  SCAN-supplied  and  user-supplied  default  values  will be
covered.  This is an  especially  important  area,  since  it  is
something  many believe should be provided by SCAN directly, that
the user program should not be forced to  become  involved  with.
Because of this, it is also important to notice when the standard
DEC SCAN is being referenced, and when the modified SCAN is being
referenced.



7.2  FILE SPEC DEFAULTS

     The "DM"  macro  gives  the  user  the  ability  to  specify
defaults,  but  the  user program must also do the enforcement of
some of those defaults.   This  is  especially  true  of  default
values  used when the switch is absent on the command line:  SCAN
will not go through  the  tables  DOSCAN  produces  to  see  what
switches  were not specified, to be able to apply the appropriate
default values.  This entire area is one of the gaping  holes  in
SCAN.



7.3  ABSENT DEFAULTS VS PRESENT DEFAULTS

     When the DM macro was introduced, the point  was  made  that
two default values are allowable.  One is the default value to be
used whenever the switch is absent from the command line  (absent
default),  and the other is the default value to be used when the
switch is given, but without an explicit value (present default).
The arguments given to DM are in the following format:

          DM    (ABBREV,MAX,ABSENT,PRESENT)

          where:

DEFAULT VALUE HANDLING                                   Page 7-2
ABSENT DEFAULTS VS PRESENT DEFAULTS                     11 Jun 79


          ABBREV is the 1-3 char name used
                  in the SL or SP macro
          MAX is the maximum value
          PRESENT is the present default
          ABSENT is the absent default

          which generate the following symbols:

          MX.ABBREV (maximum value)
          PD.ABBREV (present default)
          AD.ABBREV (absent default)



     The generated symbols are  always  global,  and  will  never
re-define  prior  values.   In other words, one can manually give
values to some of  the  symbols  to  which  DM  normally  assigns
values, then call DM, without having the manually assigned values
destroyed.

     This discussion leads one to expect that SCAN  will  perform
the  following  functions when it is processing switches, or when
it is applying default values (as in .APLST):

      o  Range  check  values  to  be  sure   they   are   within
         0<=MX.ABBREV

      o  Give PD.ABBREV as the value when only /SWITCH is seen on
         the command line

      o  Give AD.ABBREV as the value when /SWITCH is not seen  on
         the command line at all


     However, only #1 and 2 are supported by SCAN at the  present
time.   The  generation  of the AD.ABBREV symbols by DM is solely
for use by the program which is  using  SCAN.   Such  support  is
planned  for the next release of the modified DEC SCAN.  The text
below will outline the steps necessary to support this in a  user
program.  The envisioned support within the modified SCAN will be
in one of two forms:

      o  Additional code to .APLST,  so  that  all  switches  are
         defaulted  whenever  file specifications are.  It is not
         clear that this is the way to go, since it is  sometimes
         desirable  to  seperate  the  handling  of file-spec and
         non-file-spec  switches.   This  is  the   reason,   for
         instence,  for  the  existence of the FS.NFS (Not a File
         Switch) flag.

      o  The inclusion  of  an  additional  routine,  which  will
         default  the  user  switches.   This  is  the preferable
         method, and (more than likely) the  one  which  will  be
         used.

DEFAULT VALUE HANDLING                                   Page 7-3
IMPLEMENTING SUPPORT OF ABSENT DEFAULTS                 11 Jun 79


7.4  IMPLEMENTING SUPPORT OF ABSENT DEFAULTS

     This support consists of two distinct phases:  assembly time
generation of necessary table(s), and execution time code to scan
the SWTCHS tables (as well as the added  one(s)).   There  is  no
real problem or difficulty in either of these.



7.4.1  GENERATING TABLES AT COMPILE TIME

     This task will be performed immediately after the usual call
to DOSCAN, and will generate a table using the SWTCHS macro.  One
must be careful to check to see if an absent default  has  indeed
been  given for each switch.  Since the AD.ABBREV symbols are not
used for any other purpose, the problem of determining whether or
not  a switch is eligible for defaulting is conveniently avoided.
One possible macro might be the following,  which  generates  the
table "xxxxxA":

          DEFINE DODFLT(NAME),<

          DEFINE X($NAME,$PROC,$POINT,$DEFLT,$MAX,$FLAGS),<
          IFNDEF AD.'$DEFLT,<
          Z             ;$NAME - NO ABSENT DEFAULT
          >

          IFDEF AD.'$DEFLT,<
          XWD   400000,AD.'$DEFLT       ;$NAME
          >
          > ;END OF DUMMY MACRO "X" FOR SWTCHS

          NAME'A::
          SWTCHS
          > ;END OF DODFLT MACRO



     The table "xxxxxA" is organized is such a  manner  that  the
sign bit indicates whether or not an absent default is applicable
for this position's switch.  When the sign bit is on,  the  right
half  of  the same word is the absent default.  If it is off, the
rest of word is ignored.



7.4.2  EXECUTION TIME SUPPORT CODE

     The other task to be performed is the writing of code to  be
called  at about the same time .APLST is called, but AFTER .OSDFS
is called to apply .OSCAN's default  values.   The  procedure  to
follow is simple.  The following code gives a possible method.

DEFAULT VALUE HANDLING                                   Page 7-4
IMPLEMENTING SUPPORT OF ABSENT DEFAULTS                 11 Jun 79


        .APLDF::HRLZI   T1,-xxxxxL
        LOOP:   SKIPL   T2,xxxxxA(T1)
                JRST    ENDLUP
                MOVE    T3,xxxxxP(T1)

        ;determine how to store value
        ;see the code around SWDPBE in SCAN

        ENDLUP: AOBJN   T1,LOOP

        ;here with all absent defaults applied



     As this example indicates, some thought needs to be given at
the  point where the value in T2 is to be stored via the contents
of T3.  T3 can take various  forms,  although  it  is  usually  a
standard  byte  pointer.  The principle exception in this context
is when the switch allows multiple  arguments,  and  the  STORAGE
field in SWTCHS is used to specify the length and location of the
area in which to store the values.  The other  exception  is  the
case  where  a  full word is to be stored for the value, in which
case the left half of the "pointer" is zero, and the  right  half
is the location to store the value.

     As the example  also  indicated,  the  method  for  properly
handling  this  is in SCAN, in the routine SWDPBE, which is where
all values for switches are stored.  In this code, P2 is pointing
to a 4 word table containing the addresses of the tables produced
by DOSCAN.  The offsets in this table are given the names:

          SWN==0 (xxxxxN)
          SWP==1 (xxxxxP)
          SWM==2 (xxxxxM)
          SWD==3 (xxxxxD)

P1 is used to index  into  the  "xxxxx?"  tables  to  access  the
entries  for  the  current command (ie:  xxxxxN(P1) is the SIXBIT
name of the current command, etc.).   Knowing  this,  it  is  not
difficult to follow the logic of the code.



7.5  SUMMARY

     The purpose of this chapter is  to  provide  information  on
handling  default  values.   The defaults catagorized as "present
defaults," which are used whenever the switch  is  specified  but
its  value  is  not, are already handled completely by SCAN.  The
other catagory - "absent defaults" - are not handled in  any  way
be the current version of SCAN.  The method in which this will be
implemented in a future version of  the  modified  DEC  SCAN  was
presented.  In addition, the general method for implementing this
in a user program was given.













                            CHAPTER 8

                   FILE-SPECIFICATION SCANNING






 8.1  FILE-SPEC SCANNING

      An earlier section (The Command Scanners) gave  a  detailed
 description of what a file-specification is.  What is of concern
 here is the use of .FILIN, the  SCAN  routine  for  inputting  a
 file-spec.



 8.2  SCAN BLOCKS

 8.2.1  DEFINITION

      Crucial to this topic is a discussion of what is  called  a
 "Scan-Block,"  which  is SCAN's internal (mostly) representation
 of the information relevant to the file-spec which was  scanned.
 Appendix  D  ("SCNMAC")  contains  the  exact definitions of the
 words  and  bits  in  a  Scan-Block.   Generally  speaking,  the
 information includes:

    o  Device name.

    o  Filename and its mask.

    o  Extension and its mask.

    o  PPN and its mask, along with any PATH information.

    o  Selection criteria, based on switches encountered  (dates,
       times, etc.).

    o  Indications of the various switches' presence or absence.

    o  Syntax representations.


FILE-SPECIFICATION SCANNING                              Page 8-2
Scan Blocks                                             11 Jun 79


 8.2.2  SCAN'S BUILT IN SWITCHES

      The  switches  referred  to  were  mentioned   earlier   as
 "Internal SCAN Switches."  These are mostly used to specify file
 selection criteria, especially for use by WILD (see Appendix B).
 The  exact  definitions are included in Appendix E as one of the
 examples of Switch definitions.  Summarized, they are:



 /ABEFORE
 /ASINCE       - specify access-date-time criteria
 /BEFORE
 /SINCE        - specify creation-date-time criteria
 /ERNONE
 /OKNONE       - specify if no file-match is an error
 /ERPROTECTION
 /OKPROTECTION - specify if access-protection failure is an error
 /ERSUPERSEDE
 /OKSUPERSEDE  - specify if  it  is  an  error  to  overwrite  an
                 existing file
 /ESTIMATE     - specify an estimated file size
 /EXIT         - go to monitor
 /HELP         - type a help message /NOOPTION     -
 /OPTION       - control the use of options file (see "OSCAN")
 /PHYSICAL     - set the "physical only" bit on all OPENs.
 /PROTECTION   - specify the protection of a file
 /VERSION      - specify the version number of a file
 /RUN          -
 /RUNCORE      -
 /RUNOFFSET    - control the running of a new program  when  done
                 with this one (see "Routine Call Definitions.")



 8.2.3  SYNTAX REPRESENTATIONS

      "Syntax Representations" refer to bits, used  primarily  by
 WILD,  indicating  what special constructs were seen.  These are
 made up of usages of what SCAN terms "Guide Words," which are in
 a  sense  pseudo-characters.   The  legal Guide Words, and their
 pseudo-character values, are:

            'AND'  4000     'INPUT'  4005
            'OR'   4001     'OUTPUT' 4006
            'NOT'  4002     'SOURCE' 4007
            'FROM' 4004     'LIST'   4010
            'TO'   4003     'OBJECT' 4011

 These are used to  express  inter-filename  relationships  in  a
 command  string,  along  with  the concatenation operator -- the
 plus sign.  Refer to "INPUT ROUTINES - CHARACTER" in Chapter  2,
 and to Appendix D - "SCNMAC."

FILE-SPECIFICATION SCANNING                              Page 8-3
Built-in Switches; Guide Words                          11 Jun 79


 8.2.4  SCAN BLOCKS: SUMMARY

      So much for Scan-Blocks.  It is important to  realize  that
 they  exist, especially if any of the switches listed are of use
 to the program, or if the user is interfacing with  WILD  (which
 requires  Scan-Blocks  for  input).   The  .STOPB  routine  (see
 "Routine Definitions") is used to convert these blocks  to  OPEN
 and LOOKUP/ENTER blocks.




 8.3  F.EZER & P.EZER

      The Scan-Block used by SCAN is located at the global symbol
 "F.ZER",  and  extends  to  "F.EZER".  Associated with this is a
 "default region," into which the user places his default values,
 if  any,  before  calling  SCAN.  The definitions of the offsets
 into those blocks are in SCNMAC, a listing of which is  included
 in  the  appendices.   These  symbols  have  names of the format
 ".FX???".  This area extends from "P.ZER" to ".EZER", and should
 be  zeroed if no defaults exist.  To have these defaults applied
 (after SCAN has returned), one issues the call:

      PUSHJ P,.APLST##

 to apply what SCAN calls  "sticky  defaults."  This  is  covered
 future  in  a  following  Chapter,  "DEFAULT  AND  MAXIMUM VALUE
 HANDLING."

      Once the Scan block at F.ZER has had  the  user's  defaults
 applied,  then  it remains to:  1) apply SCAN's defaults, and 2)
 to move it to the user's area.  This is done  in  the  following
 manner:

      MOVEI T1, address ;user's Scan-Block address
      MOVEI T2, length ;length of same
      PUSHJ P,.GTSPC##


 After this, the area of  F.ZER  can  then  be  reused  for  more
 file-specs.



 8.4  .STOPB

      Once the scan blocks were created  by  SCAN,  and  possibly
 processed  by  WILD  (to  resolve  wild  card  expressions), the
 problem remains of  doing  something  with  them.   The  TOPS-10
 monitor   will   certainly  not  accept  them  to  specify  file
 operations.  What needs to be done is to covert  from  the  SCAN
 block  format  needed  during scanning, to the standard OPEN and
 LOOKUP/ENTER block format needed during processing.  The routine

FILE-SPECIFICATION SCANNING                              Page 8-4
.STOPB                                                  11 Jun 79


 whhich  performs  this  task  is  ".STOPB"  (Scan To OPen lookup
 Block).  The call on .STOPB is of the format:

           T1/  SCAN-block-len,,SCAN-block-address
           T2/               0,,OPEN-block-address
           T3/ LOOKUP-block-len,,LOOKUP-block-address
           T4/               0,,PATH-block-address (9 words)

           PUSHJ  P,.STOPB##
                   -error- (wildcards not yet resolved)
                   -ok- SCAN block is translated



 8.5  USING .FILIN

      Now that all else  has  been  taken  care  of,  the  actual
 scanning  of  file-specifications  is  simple  to  explain.  The
 routine responsible for this is .FILIN, which is called  in  the
 following manner:

      PUSHJ P,.FILIN##

 and returns with T1 containing:

       0 if null expression
      -1 if file spec typed
       1 if only switches seen



FILE-SPECIFICATION SCANNING                              Page 8-5
SUMMARY OF FILE SPEC SCANNING                           11 Jun 79


 8.6  SUMMARY OF FILE SPEC SCANNING

      Summarizing the file-spec scanning process,  we  have  seen
 that the following sequence is the general method used:

    o  Setup defaults in P.ZER area

    o  Call .FILIN

    o  Call .APLST

    o  Call .GTSPC

    o  Call WILD

    o  Call .STOPB

    o  Process LOOKUP/ENTER and OPEN blocks














                            CHAPTER 9

                 .ISCAN - SCANNER INITIALIZAITON






 9.1  ISCAN - SCANNER INITIALIZATION

      Before calling one of the command scanners  (or  any  input
 routine),  it  is necessary to give SCAN a set of parameters and
 other information describing how the user intends  to  go  about
 doing  things.   In "ROUTINE CALL DEFINITIONS" a skeleton format
 of an ISCAN call was  given,  which  is  sufficient  for  a  job
 interested  in doing only simple TTCALL I/O, without any frills.
 Here will be described in detail  all  of  the  various  options
 available via ISCAN.



 9.2  INITIALIZATION CONCERNS

      A number of procedures are  followed  by  SCAN  during  its
 internal  initialization,  via  ISCAN.   These  tend  to revolve
 around the one-time setting up of storage, for later  use.   The
 specific functions, which are covered in detail in the following
 paragraphs,  include:   Rescanning  the   command   line   which
 initiated the program being run, determining how the program was
 entered (CCL vs normal), what I/O routines to use, what indirect
 files  (if  any) to use, etc.  Usually, many of these are not of
 great concern, and are either omitted or defaulted to.



 9.3  RESCANNING THE COMMAND LINE

      While ISCAN is not a scanner,  it  will  sometimes  process
 part of the command line.  This occurs for programs which accept
 input on the same line as the monitor line which activated them.
 In these cases, ISCAN is given a list of the valid monitor level
 commands to look for.  It then RESCANS  the  command  line,  and
 positions  the  input  routines  to the end of that command.  On
 return, T1 indicates whether a command was actually seen or  not
 (see  call  description  below).   If  no  table  of commands is

.ISCAN - SCANNER INITIALIZAITON                          Page 9-2
RESCANNING THE COMMAND LINE                             11 Jun 79


 supplied, ISCAN will not do a RESCAN.

      One of the more common usages of this  feature  is  in  the
 writing  of  a  program  which  is  to be invoked by a spsecific
 monitor command.  When commands are added to the monitor, in the
 module  COMCON,  their  dispatch  address  in COMTAB can be to a
 routine which runs a program of the same name,, but starts it at
 the  CCL entry point (see the following paragraphs).  This makes
 it possible for a program MUMBLE to be invoked  by  commands  of
 the format:

           .MUMBLE /switch:value /switch:value ...

 In this case, .ISCAN would be told to perform the rescan of  the
 command  line,  in  order  to pick up the switches.  This is the
 process used by programs such as DIRECT.



 9.4  CCL MODE

      When a program is in what is usually termed "CCL mode,"  it
 was  started  with  an  offset  other  than 0 added to its start
 address.  In these cases, input usually comes  to  SCAN  from  a
 "CCL   file."  In  this  case,  ISCAN  must  be  told:   1)  the
 3-character CCL name, and 2) the value of the  starting  offset.
 If  not  in  CCL  mode,  then  ISCAN is given a zero word.  This
 feature is most useful for programs (such as DIRECT)  which  can
 be monitor commands.



 9.5  I/O ROUTINES

      As was stated in the Introduction, SCAN defaults to  TTCALL
 input  and  output.   If  the  user  wishes,  the address(es) of
 special routine(s) for input or output may  be  given  to  SCAN.
 Input  routines  must  leave  their  character  in  P4;   output
 routines take theirs from T1.  Neither  may  destroy  any  other
 accumulators.

      If the program knows ahead of time that indirect file input
 will  be  used, and the name of the file, then a Scan-Block form
 of the specification is passed to ISCAN.  The .FXDEV  word  must
 be non-zero for ISCAN to honor it.

.ISCAN - SCANNER INITIALIZAITON                          Page 9-3
PROGRAM TERMINATION                                     11 Jun 79


 9.6  PROGRAM TERMINATION

      Sometimes, it is useful for a program to  always  be  given
 control whenever SCAN would otherwise return to the monitor.  In
 these cases, a "MONRET" ("MONitor RETurn") address is  given  to
 ISCAN.   In  the absence of this, SCAN will simply issue an EXIT
 UUO.



 9.7  COMMAND PROMPTING

      Along  the  same  lines,  some  programs  have  their   own
 prompting  schemes,  and  must supply ISCAN with the appropriate
 address, which will later be PUSHJed to.  When it is called,  T1
 will be set up as follows:

      (RH) the normal prompt character:
            "*" for first lines
            "#" for continuation lines
      (LH) 0 for first lines;
            -1 for continuation lines

 A "continuation line" is one following a line which ended with a
 dash, which is SCAN's continuation character.



 9.8  FLAGS

      This word specifies any  special  handling  required.   The
 possible  flags  are described below, and are also listed in the
 appendices for SCNMAC and $SCNDC.

      FS.ICL - If set, whis will cause SCAN  to  "Ignore  Command
 Line" handling.  In other words, if the command line is not in a
 format SCAN understands (such as LOGIN), but  SCAN  is  used  to
 handle  parts  of  it,  the  setting  of this bit causes SCAN to
 ignore the fact that it is actually a command line.  The  RESCAN
 will still be done, however.




 9.9  CALLING .ISCAN

      This brings us now to an exact  description,  which  should
 make  sense  in  the  light  of  the preceeding paragraphs.  The
 calling format for .ISCAN is:

.ISCAN - SCANNER INITIALIZAITON                          Page 9-4
Argument Block Definition                               11 Jun 79


      MOVE  T1, [length,,argblock-address].
      PUSHJ P, .ISCAN##
        -return-

      T1 = index into table of monitor
      commands, or -1 if none found


 The argument  block  at  "argblock-address"  has  the  following
 format:


   BLOCK:
   BLOCK + 0 = 0 or IOWD length, monitor-commands
         + 1 = (RH) 0 or address of starting offset
               (LH) 0 or SIXBIT CCL name
         + 2 = (RH) 0 or address of output routine
               (LH) 0 or address of input routine
         + 3 = 0 or XWD length, indirect-Scan-Block
         + 4 = (RH) 0 or address of MONRET routine
               (LH) 0 or address of PROMPT routine
         + 5 =      FLAGS
 LENGTH==.-BLOCK













                           CHAPTER 10

                .TSCAN - THE TRADITIONAL SCANNER






 10.1  .TSCAN - THE TRADITIONAL SCANNER

      The most common command formats are  those  with:   1)  one
 output file-spec;  2) either one or more input-specs, or else no
 input spec at all;  and 3) command  switches  somewhere  on  the
 line.   This  is the type of command line which TSCAN processes.
 As well as needing to know where  DOSCAN's  tables  are,  a  few
 other issues come into play.



 10.2  /HELP

      One of the built-in "Internal Switches" listed  above  (see
 "File-Spec  Scanning")  was  /HELP.  It now becomes necessary to
 tell SCAN how to find the "HELP file" to be typed.   Four  types
 of help are possible.

    o  None

    o  Type a preset string

    o  Call a prenamed routine

    o  Call HELPER

 It is necessary for the caller to tell TSCAN which of the  above
 to use.



 10.3  POST PROCESSING OF SWITCHES

      As a command line is processed, it is often  desirable  for
 the  user  to  be  given  a  chance to clear out various storage
 areas,  before  a  new  command  line  is  processed.   This  is
 accomplished  by  passing  to  TSCAN the address of a routine to

.TSCAN - THE TRADITIONAL SCANNER                        Page 10-2
POST PROCESSING OF SWITCHES                             11 Jun 79


 PUSHJ to at the end of each line.

      Along the same lines, there is often data to be cleared  or
 reset  as each file-spec is processed.  SCAN will zero its F.ZER
 area, but the user may have other locations to worry about.   It
 may  also  want to change the P.ZER default area.  To do so, the
 user provides TSCAN with an address to PUSHJ to.



 10.4  SCAN BLOCK ALLOCATION

      In the chapter on "FILE-SPEC SCANNING,"  it  was  indicated
 that  SCAN  assembles its data within its own core (F.ZER) since
 the command line may very well contain  many  file-specs.   This
 means  that some method must exist for moving the Scan-Blocks to
 a "safer" area.  Since the input and output streams may  require
 different  handling,  the user provides TSCAN with the addresses
 of two routines which will  allocate  space  for  a  Scan-Block.
 These routines return the following information to SCAN:

      T1 = address of Scan-Block area
      T2 = length of Scan-Block area


      The P.ZER area, as  was  mentioned  earlier,  contains  the
 default  file-spec  values.  Often, information in one file-spec
 on a command line is the default for a later file-spec  on  that
 line.  Because of this, SCAN will "memorize" this information by
 copying the F.ZER information into the P.ZER area.  If the  user
 would  like control after this is done, an address to be PUSHJed
 to is passed to TSCAN.  Also, whenever SCAN  applies  the  P.ZER
 defaults,  the user may want to be called.  This is also done by
 giving TSCAN the address to be PUSHJed to.  Finally, as the SCAN
 of  a  line  is  commenced, the P.ZER area is cleared.  The user
 will then be called, if it had previously given  TSCAN  such  an
 address.



 10.5  STICKY DEFAULTS

      A "sticky" default  is  what  SCAN  terms  general  globals
 defaults  for  file  specifications.   These are applied by SCAN
 when .APLST is called.  When .TSCAN is called, the user has  the
 option  of specifying a special routine to call whenever SCAN is
 going to apply sticky defaults.  The left half of word number  6
 contains  the  addresses  of  the  routine  to  memorize  sticky
 defaults for all files, and the address of the routine to  apply
 these defaults to all succeeding file specifications:

           XWD  MEMORIZE-ADDRESS, APPLY-DEFAULTS-ADDRESS

 The other routine which may be specified it the routine to clear

.TSCAN - THE TRADITIONAL SCANNER                        Page 10-3
STICKY DEFAULTS                                         11 Jun 79


 any  sticky  defaults  at  the end of a file-spec scan.  This is
 given in the left half of word number 7:

           XWD  CLEAR-DEFAULT-ADDRESS, flags If the user  program
 has  not sticky switches of its own, then these fields should be
 left zero.  Otherwise, whenever SCAN does its own sticky default
 handling,  it will also can on the user's routine to process the
 user's sticky defaults at the same time.



 10.6  SCAN CONTROLLING FLAGS

      Although there  is  normally  only  one  output  file-spec,
 sometimes  multiple  output  specs  are quite valid.  Also, many
 programs do not care if a switch associated with one side of the
 "="  actually  appeared  on the other side.  To allow either (or
 both) of these special cases, flags are passed  to  TSCAN  which
 control  the  scanning  process.  These flags are also listed in
 Appendix D ("SCNMAC"):

      FS.MOT - Multiple output file specifications allowed.
      FS.MIO - Input and Output specifications may  be  mixed  on
               the    command    line,    regardless   of   their
               relationships position-wise to the "=" character.




 10.7  SWITCH PROCESSING

      Finally, it is sometimes the case that the user wants to be
 called whenever a switch value is to be stored, no matter how it
 was defined in SWTCHS.  To do this,  TSCAN  is  pointed  at  the
 routine  to do this.  When this routine is called, the following
 are set up:

          T1 = switch-value
          T2 = pointer into switch tables

 The routine, after doing what it may, non-skip returns  if  SCAN
 should not store the value, or skip-returns if SCAN should store
 it.  In either case, all accumulators are to be left intact.

.TSCAN - THE TRADITIONAL SCANNER                        Page 10-4
CALLING .TSCAN                                          11 Jun 79


 10.8  CALLING .TSCAN

      To call TSCAN, one first sets up an argument block  of  the
 following form:



    BLOCK + 0 = IOWD xxxxxL, xxxxxN
          + 1 = XWD xxxxxD, xxxxxM
          + 2 = XWD 0, xxxxxP
          + 3 = XWD help-type, help-address
                ;  help-type = 0 if none
                ;  = 1 if string
                ;  = 2 if subroutine
                ;if word = -1, use name in
                ;system table, and call HELPER
                ;if (LH) is greater than 77,
                ;but word is not -1, then word
                ;is the SIXBIT name to give HELPER.
          + 4 = (LH) 0 or routine to clear all answers
                (RH) 0 or routine to clear file answers
          + 5 = (LH) routine to allocate input file area
                (RH) routine to allocate output file area
          + 6 = (LH) 0 or routine to memorize defaults
                (RH) 0 or routine to apply defaults
          + 7 = (LH) 0 or routine to clear defaults
                (RH) flags:
                1B18 multiple output specs are legal
                1B19 switches may go anywhere on the line
         + 10 = (LH) 0 (reserved for future)
                (RH) 0 or routine to store switch values



 When "0" is given as an argument, then that option will  not  be
 used.  The "xxxxx" fields are from the DOSCAN argument.  To call
 TSCAN:

      MOVE T1, [LENGTH,, BLOCK]
      PUSHJ P, .TSCAN##
         -return- at end of line after
                  something was typed




 10.9  STORAGE INITIALIZATION

      When TSCAN returns, all of the switches and file-specs have
 been  processed,  and all values stored.  All switch value cells
 should have an initial value of -1.  This is because  SCAN  will
 detect attempts to give a switch more than one value on the same
 line.  Unless a user routine intervened, the first  value  would
 be  lost.  If the user wants this -- multiple values -- then the

.TSCAN - THE TRADITIONAL SCANNER                        Page 10-5
STORAGE INITIALIZATION                                  11 Jun 79


 switch must have a routine to do the  storing  itself.   In  any
 event,  -1 was chosen as an unlikely switch value, and therefore
 a reasonable initial value.

 N.B.:  Read Appendix "A" ("Notes on Using SCAN")



 10.10  SUMMARY

      This chapter has presented the use  of  SCAN's  most  often
 used  scanner  -  .TSCAN.   Much  of  what  has  been covered is
 relevant not only to .TSCAN, however,  but  also  to  the  other
 scanners being discussed in the following chapters.













                           CHAPTER 11

                OSCAN - THE OPTIONS FILE SCANNER




 11.1  OSCAN - THE OPTIONS FILE SCANNER



      It is often the case that a particular  application  has  a
 set of defaults that change somewhat from user to user.  In this
 case, it is not possible to define the defaults  via  DM,  since
 each  user  has  his  own, but they all run the same program.  A
 solution which is particularly  useful  is  called  an  "Options
 File."  This  is  a  single  file,  under  the user's PPN, which
 contains the default switch settings for that user.  Since  this
 is  feasible  for  many  programs,  all  use  the same file, but
 preface their particular lines of  defaults  with  their  names.
 Finally, it is possible for one program to have multiple, named,
 sets of defaults.




 11.2  FORMAT OF THE OPTIONS FILE

      This "Options File" is  the  file  DSK:SWITCH.INI,  on  the
 user's PPN.  Entries in SWITCH.INI are of the form:

         Program /SWITCH/SWITCH...
            or
         PROGRAM:OPTION /SWITCH/SWITCH

         where:

         PROGRAM is the program name.
         OPTION is the name of the set of defaults.  This used as
                 the value to the /OPTION:  switch in the command
                 line.
         /SWITCH are the switches and their values.

 Only switches are valid in the options file -- file-specs cannot
 be included.

OSCAN - THE OPTIONS FILE SCANNER                        Page 11-2
FORMAT OF THE OPTIONS FILE                              11 Jun 79


 11.2.1  Options List

      Only one calling parameter for OSCAN has not  been  covered
 already  under "TSCAN" -- the name(s) of options to select.  The
 program passes to OSCAN:  1) the pointer to a list of options to
 be selected, or 2) the name to be selected, or 3) 0 to imply the
 use of the program's name as the object of the selection.




 11.2.2  Argument Block

 The argument block for OSCAN closely resembles that for TSCAN:



    BLOCK + 0 = IOWD xxxxxL, xxxxxN
          + 1 = XWD xxxxxD, xxxxxM
          + 2 = XWD 0, xxxxxP
          + 3 = HELP WORD
          + 4 = OPTIONS WORD:
                SIXBIT/NAME/    or
                Z               or
                XWD   LEN,  LIST
 LENGTH==.-BLOCK



      LIST:  SIXBIT/OPT1/
             SIXBIT/OPT2/
                .
                .
                .
             SIXBIT/OPTn/
      LEN==.-LIST






 11.2.3  CALLING .OSCAN

      To call OSCAN:

      MOVE T1, [LENGTH,,BLOCK]
      PUSHJ P, .OSCAN##


OSCAN - THE OPTIONS FILE SCANNER                        Page 11-3
APPLYING DEFAULTS FOR .OSCAN                            11 Jun 79


 11.3  APPLYING DEFAULTS FOR .OSCAN

      After OSCAN returns, it is usually necessary  to  have  the
 switches  applied  to  any  file-specs which were scanned off by
 TSCAN (or VSCAN).  This is  the  purpose  of  .OSDFS,  which  is
 called in the following manner:

      MOVEI T1, location of Scan-Block
      MOVEI T2, length of Scan-Block
      PUSHJ P, .OSDFS##

 Once this has been done for any or all file-specs  desired,  the
 scanning process is complete.













                           CHAPTER 12

                 .VSCAN - THE VERB FORM SCANNER






 12.1  VSCAN - THE VERB FORM SCANNER




      In some applications, it is desirable to have  all  command
 lines  begin  with  a  keyword  which indicates some function or
 operation to be performed.  This is then followed on  succeeding
 lines  by  related  commands  and file-specs.  In this case, the
 function-word is referred to as a  "verb,"  and  the  associated
 scanner is therefore a "verb form scanner," or ".VSCAN."

      Normally, when VSCAN is used, the user enters his  switches
 one-per-line.    Although   SCAN  views  these  as  switches  no
 differently than it does with TSCAN, it appears to the user that
 he  is  actually  inputting  commands;   this is especially true
 since it is not necessary with VSCAN to include the  slash  that
 normally  indicates  a switch.  In some applications, this lends
 itself very well to user oriented dialogues.  While it would  be
 possible  for  switches  to appear on the line with the "verbs,"
 this would tend to contradict the philosophy behind using  VSCAN
 in the first place.



 12.2  USING .VSCAN

      From the  programmer's  point  of  view,  there  is  really
 nothing new for VSCAN that was not also necessary for TSCAN.


      The only new calling values in the argument block  are  the
 addresses  and lengths of the default and permanent switch areas
 for file-specs (a la P.ZER and F.ZER, respectively).

.VSCAN - THE VERB FORM SCANNER                          Page 12-2
USING .VSCAN                                            11 Jun 79


 12.2.1  Argument Block Format

      The exact argument block format for VSCAN is:

 BLOCK + 0 = IOWD xxxxxL, xxxxxN
       + 1 = XWD xxxxxD, xxxxxM
       + 2 = XWD 0, xxxxxP
       + 3 = HELP WORD
       + 4 = (LH) length of file-spec areas
             (RH) address of permanent area
       + 5 = (LH) 0 (reserved for future)
             (RH) address of default area
       + 6 = OPTION NAME, or 0 (to use program name)
 LENGTH==.-BLOCK




 12.2.2  CALLING .VSCAN

      The VSCAN call is:

      MOVE T1, [LENGTH,,BLOCK]
      PUSHJ P, .VSCAN##













                           CHAPTER 13

                  .PSCAN - THE PARTIAL SCANNER




.PSCAN - THE PARTIAL SCANNER                            Page 13-2
PSCAN & QSCAN - INTRODUCTION                            11 Jun 79


13.1  PSCAN & QSCAN - INTRODUCTION

     One of the drawbacks, in some applications, of having an all
purpose  scanner  such  as  TSCAN  is  that it does not allow any
flexability in the format of the  command  lines.   ALL  commands
must  conform  to the sytax used by SCAN.  Usually, this presents
no problem, since SCAN's syntax  is  in  itself  quite  flexable.
However, when it is necessary for the format of a command line to
be somewhat different, then another scanner is required.  This is
the  usefulness  of the so called "Partial Scanner." This scanner
tends to operate  as  a  co-operative  effort  between  the  user
program  and  SCAN.  Part of the command line is processed by the
program, and the remainder is processed by .PSCAN or .QSCAN.

     The process is simple.  Either .PSCAN or .QSCAN is called to
initialize  the scanning process, then the user program processes
the command line to whatever extent it desires.

     The routine which is normally called to handle  SCAN's  side
of  the command line handling is ".FILIN", which will pick up any
file specifications, as well as whatever switches it  encounters.
This makes for a relatively simple scanning process:

      o  Call .ISCAN to initialize everything

      o  CALL .PSCAN  to  initialize  for  partial  scanning  (or
         .QSCAN)

      o  Call whatever input routines  are  appropriate  for  the
         user's  portion  of  the  command  line (.SWDEC, .SWSIX,
         etc.).

      o  Call .FILIN to handle the rest of the command line

      o  Process the SCAN-blocks, if any, which were generated by
         .FILIN.

      o  Process the data returned by the switches scanned off by
         .FILIN




13.2  PSCAN VS QSCAN

     Throughout the discussion so far,  two  routines  have  been
referred  to  as  the partial scanners -- .PSCAN & .QSCAN.  These
operate in identical fashions, so far as use within a program  is
concerned.   Their  only  difference lies in their scope.  .PSCAN
sets up partial scanning on a  global  basis,  which  affects  as
input lines.  .QSCAN, on the other hand, affects only the current
line.  Other than this, they are used identically.

.PSCAN - THE PARTIAL SCANNER                            Page 13-3
SUMMARY                                                 11 Jun 79


13.3  SUMMARY

     The purpose of  this  chapter  has  been  to  introduce  the
concept of a partial scanner, which is sometimes very well suited
for a particular application.  In addition, instruction on  using
the  two  routines  supplied  by  SCAN -- .PSCAN and .QSCAN -- to
handle this type  of  scanning  has  been  given.   An  excellant
example  on  the  use  of  partial  scanners  is the Digital CUSP
CREDIR.  A part of this program, in fact, is included in a  later
chapter as a guide in writing programs which interface with SCAN.













                           CHAPTER 14

                         ACCESSING SCAN






 14.1  ACCESSING SCAN

 14.1.1  ASSEMBLY TIME FILES

      All of the MACROS, symbols and routine names referenced  in
 this  document are a part of SCAN and its associated files.  The
 following files are those used in the SCAN "system."

  o  UUOSYM.UNV
     MACTEN.UNV

     These define symbols used in the DEC  reference  manuals  to
     describe  UUOs  and their calling formats.  Also defined are
     useful macros, such as:  POINTR, TXxx, MOVx, etc.

     These are accessed by the MACRO-10 statement:

               SEARCH UUOSYM,MACTEN

  o  SCNMAC.UNV
     $SCNDC.UNV

     These files define macros and symbol definitions  for  SCAN.
     SL, SN, SP, SS, DM, KEYS, DOSCAN, etc, are all defined here

     SCNMAC and $SCNDC are accessed by the MACRO-10 statement:

               SEARCH SCNMAC,$SCNDC


ACCESSING SCAN                                          Page 14-2
ACCESSING SCAN                                          11 Jun 79


 14.1.2  LINK-TIME FILES


  o  SCAN.REL

     This is SCAN itself.  Contains all  code  described  herein,
     including  $SCNDC.   SCAN.REL  should  be  loaded in library
     search mode.


  o  HELPER.REL

     This is a module for the /HELP switch, and is loaded as  any
     other file.





 14.1.3  SOURCE FILES

      Sources to SCAN, SCNMAC,  HELPER,  MACTEN  and  UUOSYM  are
 currently distributed on the CUSP release tapes as:

            SCAN.MAC
            SCNMAC.MAC
            HELPER.MAC
            MACTEN.MAC
            UUOSYM.MAC

 Parts of $SCNDC and SCNMAC have been included  as  appendices  D
 and E respectively.

      The universal (.UNV) files for SCNMAC, $SCNDC,  MACTEN  and
 UUOSYM are normally kept on ersatz device "UNV:." The .REL files
 for SCAN, WILD, and HELPER are usually on device "REL:."




 14.1.4  SUMMARY

      In summary, the following would normally  be  seen  at  the
 start of a program using SCAN:

        SEARCH COLS,C,SCNMAC,$SCNDC
        .REQUEST REL:SCAN
        .REQUEST REL:WILD
        .REQUEST REL:HELPER

ACCESSING SCAN                                          Page 14-3
SEGMENT ALLOCATION                                      11 Jun 79


 14.2  SEGMENT ALLOCATION

      All of the code in SCAN is high segment;  no .LOW file will
 be  generated unless the user's program needs one.  As a general
 rule, when using the standard DEC SCAN, if any  calling  routine
 is  in  the  low-segment,  then  the  linked files should not be
 protected as "execute only" (i.e.:  166).  This is because  SCAN
 does  not  include PORTAL instructions at its entry points.  All
 of the entries in the modified  version  of  SCAN,  however,  do
 contain  PORTALs,  and  may  be  entered from low segments as an
 execute only high segment.













                           CHAPTER 15

                      EXAMPLE OF USING SCAN




EXAMPLE OF USING SCAN                                   Page 15-2
INTRODUCTION                                            11 Jun 79


15.1  INTRODUCTION

     This chapter will present two  complete  examples  of  using
SCAN  for  command  scanning.   It  will use much of the material
presented in previous chapters.  The basic purpose in this is  to
unite  the  concepts  and  routine  descriptions presented into a
cohesive structure.

     The first example chosen is from CREDIR, a Digital CUSP used
to  create directories on TOPS-10 systems.  The scanners used are
the Partial Mode scanners, .PSCAN & .QSCAN.

     A second example, from a private program, will present a use
of  .TSCAN,  which  is  by  far  the  most  popular  scanner.  By
examining  closely  both  examples,  the  reader  should  gain  a
detailed understanding of the use of SCAN.

EXAMPLE OF USING SCAN                                   Page 15-3
EXAMPLE:  CREDIR (.PSCAN/.OSCAN)                        11 Jun 79


TITLE   CREDIR -- ROUTINE TO CREATE A DIRECTORY  %2(103)
        SEARCH  C,SCNMAC        ;SET FOR UNIVERSALS
        SUBTTL  INITIALIZATION

CREDIR: TDZA    T1,T1           ;NOT CCL START
        MOVEI   T1,1            ;CCL START
        MOVEM   T1,OFFSET       ;STORE IT

        RESET                   ;RESET ANY EXTERNAL I/O

;NEXT GO INITIALIZE THE COMMAND SCANNER.  IN
;PARTICULAR, LOOK FOR A COMMAND ON THE SAME LINE OR A CCL
;FILE FULL OF COMMANDS.

        MOVE    T1,[ 2,,[IOWD  1,['CREDIR']
                        OFFSET,,'CRR']]
        PUSHJ   P,.ISCAN##      ;INITIALIZE COMMAND SCANNER



        SUBTTL  MAIN LOOP

;EACH PASS, WHETHER SUCCESSFUL OR NOT, ALWAYS
;ENDS BY RETURNING TO THE LABEL MAINLP.  THIS CAUSES THE
;PROGRAM TO START OVER AGAIN.  IT CAN BE EXITED BY THE
;USER BY EITHER A ^C OR A ^Z.  IF THE PROGRAM HAD BEEN
;INVOKED BY  A COMMAND OR CCL CALL, THEN SCAN WILL
;SIMULATE THE ^Z WHEN APPROPRIATE TO EXIT.

MAINLP: PUSHJ   P,.RUNCM##      ;HANDLE /RUN IF SET

        MOVE    T1,[ 4,,[IOWD SWTL,SWTN
                         SWTD,,SWTM
                         0,,SWTP
                         -1     ]]
        PUSHJ   P,.PSCAN##      ;INVOKE P-MODE SCANNER
          OUTSTR [ASCIZ \Create directory: \]

        CAMG    P4,[.CHEOF]     ;SEE IF EOF
        JRST    [PUSHJ P,.ALDON##  ;YES--HANDLE NORMAL CASES
                 CAMG  P4,[.CHEOF] ;THEN CHECK AGAIN
                 PUSHJ P,.MNRET##  ;YES--RETURN TO MONITOR
                 JRST  MAINLP]  ;THEN START OVER AGAIN

EXAMPLE OF USING SCAN                                   Page 15-4
EXAMPLE:  CREDIR (.PSCAN/.OSCAN)                        11 Jun 79


;HAVING INITIALIZED THE COMMAND SCAN FOR THIS LINE,
;NOW GET A FILE SPECIFICATION, WHICH MUST INCLUDE
;THE STRUCTURE AND DIRECTORY AND EXCLUDE THE FILE NAME AND
;EXTENSION.

        PUSHJ   P,.FILIN##      ;GET FILE SPEC
        JUMPN   T1,GETOPT       ;JUMP IF SOMETHING INPUT

;HERE IF NOTHING TYPED BEFORE THE SEPARATOR.  THE ONLY
;LEGAL CASES ARE /RUN AND INDIRECT.

        CAIN    P4,"@"          ;SEE IF INDIRECT
        PUSHJ   P,.GTIND##      ;YES--SETUP INDIRECT
        JUMPLE  P4,MAINLP       ;IF END OF LINE, GO DO MORE
        PJRST   E.ILSC##        ;OTHERWISE, GIVE ERROR

;NOW CHECK OPTION FILE TO SEE IF ANY DEFAULT SWITCHES.

GETOPT: JUMPG   P4,E.INCL##     ;ERROR IF MORE ON LINE
        MOVEI   T1,SPEC         ;POINT TO SPEC AREA
        MOVEI   T2,.FXLEN       ; ..
        PUSHJ   P,.GTSPC##      ;COPY TO US

        MOVE    T1,[ 4,,[IOWD SWTL,SWTN
                         SWTD,,SWTM
                         0,,SWTP
                         -1     ]]
        PUSHJ   P,.OSCAN##      ;HANDLE OPTION FILE
        JRST    GOTSOM          ;THEN PROCEED

EXAMPLE OF USING SCAN                                   Page 15-5
EXAMPLE:  CREDIR (.PSCAN/.OSCAN)                        11 Jun 79


;DEFINE SWITCH TABLE

DEFINE  SWTCHS,<
SP IN,QTAIN,.SWDEC##,QTA,FS.LRG
SP NAME,SPLNAM,SIXQWW,NUL,
SP OUT,QTAOUT,.SWDEC##,QTA,FS.LRG
>

DM NUL,1,0,0
DM QTA,.INFIN,.INFIN,.INFIN

        DOSCAN  (SWT)



;ROUTINE TO INPUT ONE WORD IN SIXBIT POSSIBLY QUOTED

SIXQWW: PUSHJ   P,.SIXQW##      ;GET STRING
        MOVE    P3,.NMUL##      ;GET FIRST WORD
        POPJ    P,              ;RETURN RESULT



GOTSOM: SKIPE   T1,FLDIAL       ;SEE IF DIALOG
        SKIPL   SPEC+.FXMOD     ;SEE IF DEVICE THIS TIME
        SKIPA                   ;OK--DO NOTHING
        MOVEM   T1,SPEC+.FXDEV  ;LAZY--DEFAULT HIS DEVICE
;fall into other code not of interest in
;this example case.

EXAMPLE OF USING SCAN                                   Page 15-6
EXAMPLE:  CREDIR (.PSCAN/.OSCAN)                        11 Jun 79


GOTDIR: MOVX    T1,FX.PRO       ;GET PROTECTION MASK
        TDNN    T1,SPEC+.FXMOM  ;SEE IF USER SET IT
        SKIPN   FLDIAL          ;OR NOT IN DIALOG
        JRST    GOTDR1          ;ALL OK--PROCEED

        MOVE    T1,[ 4,,[0
                         0
                         0
                         -1     ]]
        PUSHJ   P,.QSCAN##      ;INVOKE P-MODE SCANNER
          OUTSTR [ASCIZ \Protection: \]
        PUSHJ   P,.OCTNW##      ;GET OCTAL VALUE
        DPB     P3,[POINTR (SPEC+.FXMOD,FX.PRO)]
        JUMPG   P4,E.INCL##     ;ERROR IF MORE ON LINE

GOTDR1: SKIPGE  SPLNAM          ;SEE IF /NAME
        SKIPN   FLDIAL          ;NO--SEE IF DIALOGUE
        JRST    GOTDR2          ;YES--PROCEED
        MOVE    T1,[ 4,,[0
                         0
                         0
                         -1     ]]
        PUSHJ   P,.QSCAN##      ;INVOKE P-MODE SCANNER
          OUTSTR [ASCIZ \Name: \]
        PUSHJ   P,SIXQWW        ;GET SIXBIT NAME
        JUMPG   P4,E.INCL##     ;ERROR IF THAT'S NOT ALL
        MOVEM   P3,SPLNAM       ;SET NAME

GOTDR2: MOVS    T2,SPEC+.FXEXT  ;GET EXTENSION
        TLC     T1,-1           ;MASK SHOULD BE -1
        CAIE    T1,'UFD'        ;SEE IF UFD
        CAIN    T1,'SFD'        ; OR SFD
        SETZB   T1,SPEC+.FXEXT  ;YES--CLEAR OUT
        SKIPN   SPEC+.FXNAM     ;SEE IF FILE NAME
        SKIPE   SPEC+.FXEXT     ; OR EXTENSION
        JRST    E$$FNI          ;YES--FILE NAME ILLEGAL

        MOVEI   T1,SPEC         ;POINT TO SCANNED SPEC
        MOVEI   T2,OPNBLK       ;POINT TO AN OPEN BLOCK
        MOVEI   T3,ENTBLK       ;POINT TO AN ENTER BLOCK
        PUSHJ   P,.STOPN##      ;CONVERT SCAN'S SPEC
          JRST  E$$WCI          ;WILD CARDS ARE ILLEGAL
        JRST    DEVOK           ;PROCEED

;fall into code which does actual processing of directories,
;etc., which is of no concern here as a SCAN example.

EXAMPLE OF USING SCAN                                   Page 15-7
TSCAN Example                                           11 Jun 79


     The next example, of the use of TSCAN,  is  from  a  program
written  to count the number of form-feeds in an arbitrary set of
files.  No switches are used, but a dummy  SWTCHS  definition  is
used  to  keep TSCAN happy.  The inclusion of additional switches
would  be  trivial.   The  important  parts  to  watch  are   the
interfacing  with  TSCAN,  and the processing of the SCAN blocks.
The actual use of the converted OPEN and LOOKUP/ENTER  blocks  is
left out.

EXAMPLE OF USING SCAN                                   Page 15-8
TSCAN Example                                           11 Jun 79


TITLE   FINDFF - FIND NUMBER OF FORM-FEEDS IN GROUP OF FILES
        .REQUEST SCAN
        .REQUEST WILD
        SEARCH  UUOSYM,SCNMAC,$SCNDC

;*************************************************
; INITIALIZATION ROUTINE
;*************************************************
FINDFF: RESET
        MOVE    P,[IOWD PDLSIZ,PDL]
        MOVEI   T1,1
        MOVEM   T1,TOTFF        ;STARTS AT 1 PAGE (NO INITIAL FF)
        MOVE    T1,[ISCLEN,,ISCBLK]
        PUSHJ   P,.ISCAN##      ;INITIALIZE SCAN
        PUSHJ   P,.TCRLF##
        SETZM   WILDSW          ;INDICATE NO WILD SPEC IN FORCE

;*************************************************
; ROUTINE TO GET NEXT FILE SPECIFICATION FROM SCAN
;*************************************************

GETNAM: SKIPE   WILDSW          ;SKIP IF NO WILD SPEC IN FORCE
        JRST    CALWLD          ;JUMP IF A WILD SPEC IS CURRENT

GETSPC: MOVE    T1,[XWD P.ZER##,P.ZER##+1]
        SETZM   P.ZER##
        BLT     T1,P.EZER##     ;INIT DEFAULT REGION FOR .TSCAN
        MOVE    T1,[TSCLEN,,TSCBLK];ARGUMENT BLOCK
        PUSHJ   P,.TSCAN##      ;GET NEXT FILE SPECIFICATION 
                                ;FROM INPUT SOURCE
        SETOM   WILDSW          ;REMEMBER THAT A WILD 
                                ;SPEC IS CURRENT
        HLLZS   WLDBLK+3        ;CLEAR WILD'S POINTER
        SETZ    0,              ;FIX WILD BUG WHICH CLOBBERS 0

CALWLD: MOVEI   T1,[SCNBLK]     ;RESET SCAN BLOCK ADDRESS IN CASE
        HRLM    T1,WLDBLK       ;WE ALREADY CALLED .LKWLD BEFORE,

        MOVE    T1,[OPNBLK,,LKPBLK]
        MOVEM   T1,WLDBLK+1     ;FIX WILD BUG WHICH CLOBBERS
        MOVE    T1,[WLDLEN,,WLDBLK]     ;THIS WORD
        PUSHJ   P,.LKWLD##      ;GET NEXT FILE NAME FROM WILD
SPEC
        JRST    GETSPC          ;HERE WHEN DONE WITH WILD SPEC
        POPJ    P,

EXAMPLE OF USING SCAN                                   Page 15-9
TSCAN Example                                           11 Jun 79


;*************************************************
; PROMPT ROUTINE FOR GETFIL
;*************************************************

PROMPT: MOVEI   T1,[ASCIZ /FILE: /]
        PUSHJ   P,.TSTRG##      ;TYPE STRING
        POPJ    P,


;*************************************************
; ROUTINE TO ALLOCATE OUTPUT FILE SPACE FOR SCAN
;*************************************************

GETOUT: MOVE    T1,[XWD SCNBLK,SCNBLK+1]
        SETZM   SCNBLK
        BLT     T1,SCNBLK+SCNLEN-1
        MOVEI   T1,SCNBLK
        MOVEI   T2,SCNLEN
        POPJ    P,

EXAMPLE OF USING SCAN                                  Page 15-10
TSCAN Example                                           11 Jun 79


;***********************************************************
; DEFINITIONS AND WORKAREAS NEEDED BY SCAN AND WILD
;***********************************************************

.HELPR==:.TCRLF##               ;ELIMINATE LINK10 DIAGNOSTIC

ISCBLK: Z                       ;SCAN INITIALIZATION BLOCK
        Z
        Z                       ;DEFAULT TTY I/O ROUTINES ARE
TTCALLS
        Z
        XWD     PROMPT,MONRET   ;PROMPT ROUTINE,,MONITOR RETURN
                                ;ROUTINE
        Z
ISCLEN=.-ISCBLK

SCNBLK: BLOCK   20              ;COPY SCAN BLOCK INTO HERE
SCNLEN=.-SCNBLK

WLDBLK: XWD     [SCNBLK],0      ;SCAN-BLOCK POINTER
        XWD     OPNBLK,LKPBLK   ;OPEN AND LOOKUP BLOCKS
        XWD     SCNLEN,LKPLEN   ;LENGTHS OF SCAN BLOCK 
                                ;AND LOOKUP BLOCK
        EXP     1B0             ;ALLOW ANY DEVICE
        EXP     .POPJ##         ;NO ROUTINE TO CALL AT END OF UFD
WLDLEN=.-WLDBLK

DEFINE  SWTCHS<
SP      FOO,FOOLOC,.SIXSW##,,,0 ;DUMMY SWITCH FOR .TSCAN
>

DOSCAN  (FOO)

TSCBLK: IOWD    FOOL,FOON       ;ARGUMENT BLOCK FOR TSCAN
        XWD     FOOD,FOOM
        XWD     0,FOOD
        Z
        Z
        XWD     GETOUT,GETOUT
        Z
        Z
        Z
TSCLEN=.-TSCBLK

FOOLOC: Z













                           CHAPTER 16

                USING THE MISCELLANEOUS ROUTINES



16.1  INTRODUCTION

     The purpose of this chapter is to highlight the uses of some
of  the  miscellaneous routines in SCAN.  These are routines that
are not directly related to the task of scanning  command  lines,
but  which  often  make  writing  programs  simpler.  The initial
chapter, which listed the routines  in  SCAN,  gave  an  adequate
description  of  the Input and Output routines, which will not be
covered here.



16.2   .LKNAM

     This routine is used to perform the commonly needed task  of
table  searching.   It is, in fact, the routine which the command
scanners themselves use to lookup switch and command names.   The
argument,   which  must  be  in  SIXBIT  (like  the  table  being
searched), can be an abbreviation  of  an  entry  in  the  table.
Exact  matches  will  always be found, even if they constitute an
abbreviation for another command.  The lookup  attempt  into  the
table  will  fail  for  one  of  two  reasons:   1)  no  match or
abbreviation was found at all, or 2) more than one  abbreviation,
and no exact match, was found.

     The call on .LKNAM is as follows:

          MOVE T1,[IOWD len,address]
          MOVE T2,[SIXBIT/mumble/]
          PUSHJ P,.LKNAM##
           -here if failure-
           -here if success-


USING THE MISCELLANEOUS ROUTINES                        Page 16-2
 .LKNAM                                                 11 Jun 79


where:
          len     is the length of the table
          address is the address of the table
          mumble  is the word being searched for

On the failure return:

          T1<0 if no match was found
          T1>0 if multiple abbreviations were found

On success return:

          T1<0 if exact match was found
          T1>0 if abbreviation was found
          (RH) of T1 = address of table entry matched




16.3  DATE AND TIME CONVERSION

     Since the conversion between Universal Date/Time and the DEC
standard  format is complex, a routine is provided within SCAN to
perform this function.  The Universal format contains the date in
the  left half, and the time in the right half.  The DEC standard
Format contains the date (derived in a different manner)  in  one
word,  and  the  time (also of a different derivation) in another
unrelated word.  Three routines  are  provided  to  handle  these
functions:

      o   .CNTDT - convert from Universal to DEC

      o   .CNVDT - convert from DEC to Universal

      o   .GTNOW - get the current time in Universal format




16.3.1   .CNTDT

     To convert from universal format  to  DEC  format,  use  the
following calling specification:

          MOVE T1,universal date-time
          PUSHJ P,.CNTDT##
           -always returns here-


USING THE MISCELLANEOUS ROUTINES                        Page 16-3
DATE AND TIME CONVERSION                                11 Jun 79


          with T1=time as MS past midnite
           and T2=DEC format date



16.3.2   .CNVDT

     This routine converts from DEC format to  Universal  format.
The calling sequence for it is:

          MOVE T1,time
          MOVE T2,date
          PUSHJ P,.CNVDT##
           -always returns here-

where
          "time" is the time in milleseconds past midnite
          "date" is the date in DATE UUO format

On return,

          T1=Universal date/time, or
          T1=-1 if arguments were past Sept.  27,2217

An advantage of the Universal format is the  ease  of  converting
from  date  to  day  of week.  The base for the Unviersal system,
also referred to as the Astronomical Standard, was  a  Wednesday.
Therefore, dividing the Universal date by seven yields a remainer
that indicates the day of the week.  Zero would be  a  Wednesday,
and the others fall in sequence.



16.3.3   .GTNOW

Since the only method of finding the current Universal  date/time
from  the  monitor if via a GETTAB, life is made a little simpler
by using this routine.  It takes no arguments, and simply returns
the current date and time in universal format, in T1.



16.4  MANIPULATING LISTS OF DATA

     SCAN provides two routines useful when a list of  data  must
be  manipulated  in a sequential fashion.  One routine is used to
remove a data word from the list, another to place data into  the
list.

     The accumulator usage for these routines is a follows:

      o  T1 is the current address in the list

USING THE MISCELLANEOUS ROUTINES                        Page 16-4
MANIPULATING LISTS OF DATA                              11 Jun 79


      o  T2 is the number of words left in the list

      o  T3 is the data being manipulated.


     To place data  into  the  list,  .PTWRD  is  called  in  the
following manner:

          MOVE T1,address
          MOVE T2,length
          MOVE T3,datum
          PUSHJ P,.PTWRD##
           -always returns here-

with

          T1 incremented to the next list address
          T2 decremented by 1
          T3 contains the old data item


     To remove an item from the  list,  .GTWRD  is  called  in  a
similar fashion:

          MOVE T1,address
          MOVE T2,length
          PUSHJ P,.GTWRD##
           -always returns here-

with

          T1 incremented by 1 to the next location
          T2 decremented by 1
          T3 data item, or
             zero if nothing left in list (T2<=0)

Note that since the routines automatically update their pointers,
the  setup need only be done for the first usage of the routines.
After that, they can be called successively to  remove  arguments
(or  whatever)  from  a  list,  and  to  place  return values (or
whatever) into the list.













                           APPENDIX A

                   NOTES ON USING THE SCANNERS













                           APPENDICES










 A.  NOTES ON USING THE SCANNERS
 B.  NOTES ON USING WILD
 C.  DIFFERENCES BETWEEN DEC AND OLS
     SCAN AND WILD
 D.  SCNMAC - COMMAND SCANNER MACROS
 E.  $SCNDC - COMMAND SCANNER DECLARATIONS
 F.  EXAMPLE:  SCAN
 G.  EXAMPLE:  ALKFIL
 H.  LIST OF CUSPS AND THE SCANNERS WHICH
     THEY USE

NOTES ON USING THE SCANNERS                              Page A-2
                                                        11 Jun 79


  o  When supplying a user-written character input  routine,  the
     character  must  be  returned  in  P4.  No other accumulator
     should be altered.

  o  When supplying  a  user-written  routine  for  processing  a
     switch,  SCAN  will  call it via a PUSHJ, with P1 containing
     the index into the tables generated by DOSCAN for the switch
     being  processed.   If  it  is  desired  that SCAN store the
     value, then the routine must leave the value in P3, and take
     a  skip-return.   A non-skip return to SCAN is an indication
     that SCAN should not store a value.

  o  Initial values of  the  locations  into  which  SCAN  stores
     switch values should be -1.

  o  The maximum value handled by DM is 3777777;  the minimum  is
     0.   If these are not suitable for a switch, then define the
     appropriate symbols before calling DM.

  o  SCAN will  generate  a  reference  to  the  external  symbol
     ".HELPR".     This   is   normally   resolved   by   loading
     REL:HELPER.REL, and is used for processing the /HELP switch.
     However,  if  no  help  processing  is  to be done, then the
     following is sufficient:

                        .HELPR==:.TCRLF##














                           APPENDIX B

                       NOTES ON USING WILD








      For the most part, WILD is well documented in its  write-up
 in  the  Software Notebooks.  However, there are a few things to
 be aware of.

   1.  WILD has a bug  which  clobbers  AC0  in  a  very  orderly
       fashion;  try to keep your own AC0 safe.

   2.  Because of the nature of #1, if multiple  top-level  calls
       to  WILD  are  made  (i.e.:   multiple wild card specs not
       scanned  off  together),  then  WILD,   after   completely
       expanding  the  first spec, will forever after think it is
       done.  This is because AC0 is  clobbered  to  a  file-spec
       pointer,  later  to  something  else,  and then even later
       looked at in the context  of  a  file-spec  pointer.   The
       "fix"  is  a simple SETZ of AC0 before each top-level call
       to .LKWLD is started.

   3.  The documentation says that .LKWLD only needs to be  given
       the  address  of  its argument block.  WRONG!  Like almost
       all other code, it expects to see a  length  in  the  left
       half of T1.

   4.  For an unknown reason, WILD will, on occasion, write  into
       part  of its argument block, usually to the OPEN block and
       LOOKUP block pointers.  Beware.







NOTES ON USING WILD                                      Page B-2
                                                        11 Jun 79


      The  following  subroutines  are  also  documented  in  the
 Software  Notebooks,  but  are included here for added exposure.
 To type a standard LOOKUP or ENTER error message, the  following
 routines are quite useful:


  o  To type out a message which  includes  the  filename,  error
     code, etc.:

          MOVEI T1, address of extended LOOKUP/ENTER block
          MOVEI T2, length of LOOKUP block
          MOVEI T3, address of SCAN block
          PUSHJ P, E.LKEN##


  o  To type out only the code  and  its  meaning  (no  filename,
     etc.):

          MOVE1 T1, error-code
          PUSHJ P, .LKERR##














                           APPENDIX C

                   CHANGES MADE TO SCAN & WILD








             Differences In SCAN & WILD Between the
                 Digital Equipment Corp. Version
                               and
                  On-Line Systems, Inc. Version






      For the most part, no major changes have been made  to  the
 DEC  released  versions.   Some  code  has  been  added, and the
 characteristics of other code have been  slightly  altered.   In
 particular:


    o  Modules for Space Allocation and Random Number  Generation
       have been added to SCAN.

    o  The subroutine .TRDXW in  SCAN  has  been  fixed  to  work
       correctly.   The  digits A,B,C,D,E,F,...  used to come out
       one digit too high (B,C,D,E,F,G,...).

    o  Code has been added to save any "T" accumulator into which
       a  value  is  not  being returned.  (DEC clobbered the "T"
       accumulators at will, since they were "temporarY").   This
       makes it simpler to use SCAN with existing software, which
       may  have  a  more  or  less  arbitrary  set  of  register
       conventions.

    o  A number of additional  single-character  output  routines
       have  been  added.   These  perform the task of printing a
       single special character, in the same way that  .TCOLN  is
       used  to  easily  print  a  colon character.  The routines
       which have been added are identifiable in the  list  given

CHANGES MADE TO SCAN & WILD                              Page C-2
                                                        11 Jun 79


       earlier  (see  Chapter Two) by the asterisk in the outside
       margin.














                           APPENDIX D

                 SCNMAC:  COMMAND SCANNER MACROS








      This is a listing of the contents of SCNMAC.MAC,  which  is
 the  file  containing  most of the MACROS and parameters used by
 SCAN's routines.  It is accessed by the

           SEARCH SCNMAC

 statement at the beginning of a program using SCAN.


                 SCNMAC - COMMAND SCANNER MACROS



        SUBTTL  COMMAND SCANNER MACROS %7(105) 25-AUG-74
  
  
  ;MACRO DEFINITIONS OF GENERAL USE
  
  ;DEFAULTS
  
  ;DM ABBREVIATION,MAX,ADEFAULT,PDEFAULT
  ;  DEFINES SYMBOLS MX.ABBREVIATION,
  ;  AD.ABBREVIATION, AND PD.ABBREVIATION TO
  ;  BE THE MAXIMUM ALLOWED VALUE, THE
  ;  DEFAULT IF THE KEYWORD IS ABSENT, AND
  ;  THE DEFAULT IF THE KEYWORD IS PRESENT
  ;  RESPECTIVELY UNLESS THE CORRESPONDING
  ;  SYMBOL IS ALREADY DEFINED.
  
  
   DEFINE       DM(ABBR,MAX,ADEF,PDEF),<
        ND      MX.'ABBR,MAX
                ND      AD.'ABBR,ADEF
                ND      PD.'ABBR,PDEF>
  

SCNMAC:  COMMAND SCANNER MACROS                          Page D-2
                                                        11 Jun 79


  
  ;  KEYS (NAME,LIST) WILL DEFINE A LIST OF KEYS BY NAME NAME
  ;     NAME CAN BE UP TO 4 CHARS.  (DEFINES NAME.T AND NAME.L)
  ;     LIST IS SIXBIT NAMES SEPARATED BY COMMAS.
  ;     DEFINES NAME CONCATENATED WITH START OF ITEM IN LIST
  ;     AS INDEX IN LIST UNLESS THE ITEM BEGINS WITH "*"
  
  
  
  
  
    ;SWITCH SCANNING MACROS AND TABLES
  
  ;  SWTCHS IS THE MACRO LISTING ALL KNOWN
  ;  SWITCHES.  IT INCLUDES THE NAME AND
  ;  STORAGE LOCATION FOR VALUE TYPES, IT
  ;  ALSO HAS THE MAX AND DEFAULT AND
  ;  PROCESSOR FOR KEY-VALUE TYPES, IT POINTS
  ;  TO THE KEYS AND HAS THE DEFAULT IF ANY
  ;  FOR STAND-ALONE TYPES, IT HAS THE VALUE.   
  ;WHEN THE SWITCH SCANNING TABLES ARE TO BE BUILT, INVOKE
  ;THE MACRO DOSCAN WITH 5-CHAR ARGUMENT TO USE AS SYMBOL PREFIX
  ;IT WILL DEFINE XXXXXN,L,P,M,D
  
  

SCNMAC:  COMMAND SCANNER MACROS                          Page D-3
                                                        11 Jun 79


  ;  SL NAME,STORAGE,TABLE-NAME,DEFAULT,FLAGS
  ;     DEFINES A LIST OF KEY-VALUES (SEE KEYS MACRO)
  ;     DEFAULT IS THE ORDINAL OR 0 IF NO DEFAULT
  ;     IF LH(STORAGE)=7777B11, STORAGE = ROUTINE TO PROCESS
  ;
  ;  SP NAME,STORAGE,PROCESSOR,ABBREVIATION,FLAGS
  ;     DEFINES A VALUE PARAMETER WHOSE DEFAULTS
  ;      ARE DEFINED AT THE BEGINNING OF THE PROGRAM
  ;      BY "DM" USING THE SAME ABBREVIATION
  ;     PROCESSOR IS THE JUMP ADDRESS IN SWITCH PROCESSING
  ;      IT WILL BE CALLED WITH P1=SWITCH OFFSET IN TABLE
  ;      AND P2=POINTER TO 4-WORD BLOCK OF
  ;      INTERNAL OR EXTERNAL STUFF
  ;     IF MAX=0 AND FS.LRG, THEN ANY VALUE CAN BE STORED
  ;      ELSE, 0.LE.VALUE.LE.MAX
  ;
  ;     0.LE.MAX,DEFAULT.LT.2**17 UNLESS FS.LRG
  ;
  ;     IF MAX=0 AND NOT FS.LRG, THEN
  ;     PROCESSOR IS AN IMMEDIATE ACTION
  ;      WHICH WILL ALWAYS BE CALLED
  ;      ELSE, PROCESSOR WILL BE CALLED ONLY IF ":"
  ;
  ;  SS NAME,STORAGE,VALUE,FLAGS
  ;     DEFINES A STAND-ALONE PARAMETER
  ;
  ;     IN ALL CASES, STORAGE IS A BYTE POINTER.
  ;      IF A FULL WORD, ONLY THE ADDRESS IS NEEDED
  ;      IF A MULTIPLE WORD, THE BYTE SIZE IS 65-#WORDS
  ;      (UP TO 28)
  ;      IF A FILE SPECIFICATION, THE LENGTH IS HELD
  ;      IN MX.ABBREVIATION
  ;      IF POINTER IS 7777??,,??????  THEN RH(POINTER)
  ;      IS DISPATCH ADDRESS OF PROCESSOR WHICH TAKES
  ;      KEYWORD SWITCH VALUES
  ;
  ;  SN NAME,STORAGE,FLAGS
  ;     DEFINES A STAND-ALONE PARAMETER WHICH TAKES VALUE
  ;      1 IF /NAME, AND VALUE 0 IF /NONAME
  
  ;FLAGS WHICH CAN BE DEFINED IN SWITCH TABLE
  >FS.NFS==1B0  ;THIS SWITCH IS NEVER PART OF A
                ;FILE SPECIFICATION
                ;  THIS SHOULD BE SET ON GLOBAL SWITCHES
                ;  ** VERY IMPORTANT TO GET RIGHT **
  >FS.LRG==1B1  ;THE MAX AND DEFAULT VALUES ARE 0 OR .GT.  2**17
  >FS.NUE==1B2  ;NO USER EXIT ON THIS SWITCH
  >FS.VRQ==1B3  ;VALUE REQUIRED
  >FS.OBV==1B4  ;OR BIT VALUES TO RIGHT HALF
  >FS.NOS==1B5  ;SWITCH TAKES "NO" PREFIX
                ;(INTERNAL FOR SN MACRO ONLY)
  >FS.NCM==1B6  ;SWITCH DOES NOT CONSTITUTE A COMMAND [102]
                ;  (FOR /RUN, /OPTION, /EXIT)
  

SCNMAC:  COMMAND SCANNER MACROS                          Page D-4
                                                        11 Jun 79


  ;WORDS IN FILE SPEC AREA
  .FXDEV==0     ;DEVICE (NON-ZERO IF ANY PART OF SPEC)
  .FXNAM==1     ;NAME (NON-ZERO IF NAME PRESENT)
  .FXNMM==2     ;NAME MASK
  .FXEXT==3     ;EXTENSION,,EXTENSION MASK (NON-ZERO DOT PRESENT)
  .FXMOD==4     ;MODIFIER WORD
  .FXMOM==5     ;MODIFIER MASK
  .FXDIR==6     ;DIRECTORY WORD (EACH HALF=0 IF DEFAULT;
                ;SFD:0 IF END)
  .FXDIM==7     ;DIRECTORY MASK
  .FXBFR==22    ;/BEFORE
  .FXSNC==23    ;/SINCE
  .FXABF==24    ;/ABEFORE
  .FXASN==25    ;/ASINCE
  .FXFLI==26    ;FILE MIN SIZE (WORDS)
  .FXFLM==27    ;FILE MAX SIZE (WORDS)
  .FXEST==30    ;/ESTIMATE
  .FXVER==31    ;/VERSION
  
  ;LENGTHS OF FILE SPEC AREA
  .FXLEN==32    ;LENGTH OF ONE SPECIFICATION
  .FXLND==6     ;LENGTH OF DIRECTORY (UFD+SFD'S)
  
  ;BYTES IN SCAN MOD WORD
  FX.NDV==1B0   ;NULL DEVICE
  FX.NUL==1B1   ;NULL EXTENSION
  FX.DIR==1B2   ;DIRECTORY SPECIFIED (MOD=0 IF [-])
  FX.PHY==1B3   ;/PHYSICAL
  FX.NOM==1B4   ;/OKNONE
  FX.DFX==1B5   ;DIRECTORY DOES NOT NEED FIX-UP BY WILD
  FX.TRM==7B8   ;CODE FOR SPEC'S TERMINATION
        .FXTRA==1       ;& (AND)
        .FXTRO==2       ;!  (OR)
        .FXTRN==3       ;- (NOT)
        .FXTRC==4       ;+ (CONCATENATE)
  FX.STR==1B9   ;/STRS
  FX.PRT==1B10  ;/OKPROT
  FX.SUP==1B11  ;/ERSUPERSEDE
  
  FX.DEN==7B23  ;/DENSITY       [105]
  FX.PAR==1B24  ;/PARITY
  FX.PRO==777B35        ;/PROTECTION
  

SCNMAC:  COMMAND SCANNER MACROS                          Page D-5
                                                        11 Jun 79


  ;SPECIAL CHARACTERS FOR SCAN
  .CHALX==0     ;ALTMODE
  .CHEOL==-1    ;END OF LINE
  .CHEOF==-2    ;END OF FILE
  
  ;GUIDE WORDS (TURNED INTO PSEUDO CHARACTERS)
  
  .CHAND==4000  ;'AND'                                  [101]
  .CHOR==04001  ;'OR'                                   [101]
  .CHNOT==4002  ;'NOT'                                  [101]
  .CHTO==04003  ;'TO'                                   [103]
  .CHFRM==4004  ;'FROM'                                 [103]
  .CHINP==4005  ;'INPUT'                                [103]
  .CHOUT==4006  ;'OUTPUT'                               [103]
  .CHSRC==4007  ;'SOURCE'                               [103]
  .CHLST==4010  ;'LIST'                                 [103]
  .CHOBJ==4011  ;'OBJECT'                               [103]
  
  
  ;FLAGS FOR .ISCAN CALL
  
  FS.ICL==1B17  ;IGNORE SPECIAL COMMAND-LINE HANDLING
  
  ;FLAGS FOR .TSCAN CALL
  
  FS.MOT==1B18  ;MULTIPLE OUTPUT SPECS POSSIBLE
  FS.MIO==1B19  ;MIXED INPUT AND OUTPUT SPECS
  
  ;FLAGS FOR .TDIRB CALL
  
  TS.DRW==0     ;SINGLE WORD
  TS.DRP==1     ;PATH POINTER
  TS.DRB==2     ;BIWORD (IE, SCAN SPEC FORMAT)
  
  ;VALUES FROM .VERBO
  
  JWW.CN==1B33  ;/VERBOS:CONTINUATION
  JWW.FL==1B34  ;/VERBOS:FIRST
  JWW.PR==1B35  ;/VERBOS:PREFIX













                           APPENDIX E

              $SCNDC:  COMMAND SCANNER DECLARATIONS








$SCNDC is a part of SCAN.MAC, which generates $SCNDC.UNV whenever
SCAN is assembled.  It contains the definitions of some SCAN/WILD
related symbols, and the accumulators, for use by programs  which
must interface with SCAN & WILD.  It is accessed by the

          SEARCH $SCNDC

statement at the beginning of the program using SCAN or WILD.





 
 
        UNIVERSAL $SCNDC -- DECLARATIONS FOR COMMAND SCANNER
        SEARCH  C,SCNMAC        ;SEARCH PARAMETERS FOR THIS FILE
 
 ;AC NAMES
 
 T1=1           ;TEMPORARIES
 T2=2
 T3=3
 T4=4
 
 P1=5           ;PRESERVED ACS FOR CALLING ROUTINES
 P2=6
 P3=7
 P4=10
 
 P=17           ;PUSH-DOWN POINTER
 
 
 DM MSG,77777,0,7       ;MESSAGE
 DM PRO,777,0,277       ;PROTECTION

$SCNDC:  COMMAND SCANNER DECLARATIONS                    Page E-2
                                                        11 Jun 79


 DM RNC,777777,0,0      ;RUN CORE
 DM RUN,7,-1,1          ;RUN OFFSET
 
 VRBADX==10             ;/MESSAGE:ADDRESS
 
 PRGEND













                           APPENDIX F

            EXAMPLES:  SCAN'S INTERNAL SWITCH TABLES








It was mentioned at various points in  the  text  that  SCAN  has
certain  switches built into it.  As might be expected, SCAN uses
itself to process htese switches.  Therefore, it  is  interesting
and  useful  to see just how SCAN defines its own switches, using
the DOSCAN, SWTCHS, DM and KEYS macros.





 
 
 
 
 ;HERE WE DEFINE STANDARD SWITCHES PROCESSED IN SCAN
 
        DEFINE  SWTCHS,<
 SP ABEFORE,F.ABF,.SWDTP,,FS.VRQ
 SP ASINCE,F.ASN,.SWDTP,,FS.VRQ
 SP BEFORE,F.BFR,.SWDTP,,FS.VRQ
 SL DENSITY,<POINTR (F.MOD,FX.DEN)>,DENS,DENSIN
 SS ERNONE,<POINTR (F.MOD,FX.NOM)>,0
 SS ERPROTECTION,<POINTR (F.MOD,FX.PRT)>,0
 SS ERSUPERSEDE,<POINTR (F.MOD,FX.SUP)>,1
 SP ESTIMATE,F.EST,.BLOKW,,FS.VRQ
 SP EXIT,N.DEV,SWEXIT,,FS.NFS!FS.NCM
 SL *HELP,<-1,,.SWHLP>,HELP,HELPTEXT,FS.NFS!FS.NCM
 SP LENGTH,F.FLM,SWLEN,,FS.VRQ
 SL MESSAGE,<*F,.FLVRB##>,VRB,PD.MSG,FS.OBV!FS.NFS!FS.NCM
 SS NOOPTION,OPTION,0,FS.NFS!FS.NCM
 
 SS OKNONE,<POINTR (F.MOD,FX.NOM)>,1
 SS OKPROTECTION,<POINTR (F.MOD,FX.PRT)>,1
 SS OKSUPERSEDE,<POINTR (F.MOD,FX.SUP)>,0
 SP OPTION,OPTION,.SWSIX,OPT,FS.NFS!FS.NCM

EXAMPLES:  SCAN'S INTERNAL SWITCH TABLES                 Page F-2
                                                        11 Jun 79


 SL PARITY,<POINTR (F.MOD,FX.PAR)>,PAR,PARODD
 SN PHYSICAL,<POINTR (F.MOD,FX.PHY)>
 SP PROTECTION,<POINTR (F.MOD,FX.PRO)>,.SWOCT,PRO
 SP RUN,N.ZER,.SWFIL,RNL,FS.NFS!FS.NCM!FS.VRQ
 SP RUNCORE,N.CORE,.SWCOR,RNC,FS.LRG!FS.NFS!FS.NCM
 SP RUNOFFSET,N.OFFS,.SWOCT,RUN,FS.NFS!FS.NCM
 SP SINCE,F.SNC,.SWDTP,,FS.VRQ
 SN STRS,<POINTR (F.MOD,FX.STR)>
 SP TMPFILE,,SWTMP,,FS.VRQ!FS.NFS!FS.NCM
 SP VERSION,F.VER,.VERSW,,FS.VRQ
 >
 

EXAMPLES:  SCAN'S INTERNAL SWITCH TABLES                 Page F-3
                                                        11 Jun 79


 ;NOW BUILD THE TABLES FROM THE SWTCHS MACRO
        MX.OPT==1
        PD.OPT==0
        MX.RNL==N.EZER-N.ZER+1
        PD.RNL==0
 
 
        DOSCAN  (STSWT)
 
 
 ;HERE WE BUILD THE KEYS
 
 KEYS (DENS,<200,556,800,1600,6250,%%,$$,INSTALLATION>)
 KEYS (HELP,<SWITCHES,TEXT>)
 KEYS (PAR,<EVEN,ODD>)
                                ;  --DUMMIES--          [321]
 KEYS (VRB,<PREFIX,FIRST,CONTINUATION,$$,$%,%$,%%,ADDRESS>)
 













                           APPENDIX G

                        EXAMPLES:  ALKFIL








ALKFIL is a non-DEC program written to perform the tasks of  file
space allocation.  It uses SCAN to process the command lines, and
is a useful example of the various options available to the  SCAN
& WILD user.





 
 DEFINE SWTCHS<
 SP     SIZE,FILSIZ,.DECNW##,FIL,FS.VRQ!FS.NCM          ;[#46]
 SP     MINDRIVES,MINDRV,.DECNW##,MND,FS.VRQ!FS.NFS     ;[#51]
 SP     MAXDRIVES,MAXDRV,.DECNW##,MND,FS.VRQ!FS.NFS     ;[#51]
 SP     PARTITIONS,PARTNS,GETPRT##,PRT,FS.VRQ!FS.NFS
 SP     REPEAT,RPTFCT,.DECNW##,RPT,FS.VRQ!FS.NFS        ;[#33]
 SL     SPLIT,SPLIND,SPLT,,FS.VRQ!FS.NFS
 SL     ALLOCATE,ALCIND,ALOC,,FS.VRQ!FS.NFS
 SL     ADDRESSING,ADRIND,ADRS,,FS.VRQ!FS.NFS
 SP     BUFSIZ,BUFSIZ,.DECNW##,BUFS,FS.VRQ!FS.NFS
 SP     UNIT,UNINAM,GETUNI##,,FS.VRQ!FS.NFS             ;[#25]
 SP     BLOCK,BLKNUM,GETBLK##,,FS.VRQ!FS.NFS            ;[#23]
 SP     LBN,LBNNUM,GETLBN##,,FS.VRQ!FS.NFS              ;[#31]
 SP     STATUS,STSOBJ,.SIXSW##,,FS.NFS                  ;[#25]
 SS     STRSTS,<POINTR(F,F.STRS)>,1
 SS     CREATE,<POINTR(F,F.CREA)>,1
 SS     PREALLOC,<POINTR(F,F.PRAL)>,1
 SS     COPY,<POINTR(F,F.COPY)>,1
 SS     NOLOG,<POINTR(F,F.NLOG)>,1                      ;[#46]
 SP     SPOOL,SPOOL,.SIXSW##,,FS.VRQ!FS.NFS             ;[#57]
 SS     DEBUG,<POINTR(F,F.DEBG)>,1                      ;[#60]
 >
 
 

EXAMPLES:  ALKFIL                                        Page G-2
                                                        11 Jun 79


 ;EXPAND SWITCH TABLES FOR SCAN:
 DOSCAN(SWIT)
 
 
 ;DEFINE DEFAULTS AND KEY-LISTS
 
 ;      NAME,MAX,ABSENT-DEFAULT,PRESENT-DEFAULT
 DM     (MND,^D31,1,1)                          ;[#51]
 DM     (MXD,^D32,32,32)                        ;[#51]
 DM     (PRT,^D65,^D30,1)                       ;[#65]          
;0 IMPLIES MINIMUM NEEDED
 INTERNAL       MX.PRT,AD.PRT                   ;[#43] FOR USE
                                                ;[#43] BY OTHER
                                                ;[#43] MODULES
 DM     (RPT,1,1,1)                             ;[#32]
 DM     (BUF,^D100,^D25,^D5)                    ;[#52]
 DM     (FIL,377777,^D1000,^D1000)              ;[#40]
 
 
 ;******** IMPORTANT *********
 ;IF THE ORDER OF ARGUMENTS TO THE KEYS MACRO
 ;IS CHANGED, THEN THE CORRESPONDING $$XXX
 ;TABLE MUST ALSO BE CHANGED.
 
 KEYS   (SPLT,<BEST,LINEAR,PROMPT>)     ;[#61]
 KEYS   (ALOC,<SPACE,PHYSICAL,LOGICAL,PROMPT>) ;[#60]
 KEYS   (ADRS,<FIRST,PROMPT>)           ;[#22]













                           APPENDIX H

                     CUSPS & THEIR SCANNERS








Not all DEC programs use SCAN & WILD.  Most of  the  more  recent
(from  about  1976 on) tend to use it, and some of the older ones
use it.  Many of the remaining programs, especially the very  old
CUSPS  (REACT,  SOUP,  etc.)  each have their own code to process
their own (usually different) styles of commands.  The list  that
follows indicates which DEC (and some non-DEC) programs use SCAN,
and which use their own scanners.  It should proves useful  as  a
source  of further information on using scan.  In particular, the
module LNKSCN of LINK-10 is an excellant reference to  using  the
switch-defining macros.





CUSP            SCANNER         COMMENTS
----------      ------------    -----------------------


ALGOL           own
BACKUP          SCAN            .VSCAN
BASIC           own
BATCON (MPB)    own
BATCON (GALAXY) SCAN
BLISS-10        own             Compiler fake's it (no SFDs)
BOOT11          own
CHANGE          own
COBOL           own
COMPIL          own
CREDIR          SCAN            Uses .PSCAN

CUSPS & THEIR SCANNERS                                   Page H-2
                                                        11 Jun 79


CUSP            SCANNER         COMMENTS
----------      ------------    -----------------------


CREF            own
DAEMON          old SCAN        Has SCAN V2 built into it
DIRECT          SCAN
FILCOM          own
FILEX           own
FORTRAN-10      SCAN
GALAXY          SCAN            All components
HELP            SCAN
INITIA          own             even simulates .OSCAN
ISAM            own
JQ              SCAN            (non-DEC)  uses .TSCAN
KJOB (MPB)      own
LIBARY          own
LINED           own
LINK-10         SCAN            Excellant example (LNKSCN)
LOGIN           SCAN
LOGOUT (MPB)    own
LOGOUT (GALAXY) SCAN
LPTSPL (MPB)    own             Same for other spoolers
LPTSPL (GALAXY) SCAN            -dittoe-
MACRO           own
MAIL            own             (non-DEC) good job of faking it
MAKLIB          SCAN
OMOUNT          own
OPSER           own
PIP             own
QUEUE (MPB)     SCAN            .TSCAN
QUEUE (GALAXY)  SCAN            .TSCAN
REACT           own
RERUN           own
RUNOFF          SCAN            .TSCAN
SETSRC          own
SORT-10         SCAN
SOS             own
SOUP            own
SYSTAT          own
TECO            own
UMOUNT          own













                           APPENDIX I

                               INDEX




                                                     Page Index-1



                              INDEX




 $scndc . . . . . . . . . . . . . E-1
 .aplst . . . . . . . . . . . . . 7-2
 .ascqw . . . . . . . . . . . . . 2-6
 .asqcq . . . . . . . . . . . . . 2-6
 .blokc . . . . . . . . . . . . . 2-9
 .blokw . . . . . . . . . . . . . 2-9
 .ch??? symbols . . . . . . . . . D-5
 .clrbf . . . . . . . . . . . . . 2-13
 .cntdt . . . . . . . . . . . . . 2-11
 .cnvdt . . . . . . . . . . . . . 2-11
 .corec . . . . . . . . . . . . . 2-9
 .corew . . . . . . . . . . . . . 2-9
 .datic . . . . . . . . . . . . . 2-6
 .datif . . . . . . . . . . . . . 2-7
 .datig . . . . . . . . . . . . . 2-7
 .datim . . . . . . . . . . . . . 2-6
 .datip . . . . . . . . . . . . . 2-6
 .datiq . . . . . . . . . . . . . 2-6
 .decnc . . . . . . . . . . . . . 2-6
 .decnw . . . . . . . . . . . . . 2-6
 .filin . . . . . . . . . . . . . 2-10, 6-2
 .fx??? offsets . . . . . . . . . D-4
 .gtnow . . . . . . . . . . . . . 2-11
 .gtwds . . . . . . . . . . . . . 2-2
 .gtwrd . . . . . . . . . . . . . 2-13
 .iscan . . . . . . . . . . . . . 2-1, 9-1, D-5
 .iscan flags . . . . . . . . . . D-5
 .islgi . . . . . . . . . . . . . 2-14
 .lknam . . . . . . . . . . . . . 2-11, 16-1
 .mkmsk . . . . . . . . . . . . . 2-14
 .mkpjn . . . . . . . . . . . . . 2-11
 .namec . . . . . . . . . . . . . 2-6
 .namew . . . . . . . . . . . . . 2-6
 .octnc . . . . . . . . . . . . . 2-6
 .octnw . . . . . . . . . . . . . 2-6
 .oscan . . . . . . . . . . . . . H-2
 .pop4t . . . . . . . . . . . . . 2-2
 .popj  . . . . . . . . . . . . . 2-2
 .popj1 . . . . . . . . . . . . . 2-2
 .pscan . . . . . . . . . . . . . 13-1, 15-3, H-1
 .psh4t . . . . . . . . . . . . . 2-2
 .ptwrd . . . . . . . . . . . . . 2-13
 .qscan . . . . . . . . . . . . . 13-1, 15-3
 .rand  . . . . . . . . . . . . . 2-11
 .randm . . . . . . . . . . . . . 2-11
 .reeat . . . . . . . . . . . . . 2-13
 .runcm . . . . . . . . . . . . . 2-11
 .savex . . . . . . . . . . . . . 2-2
 .savxt . . . . . . . . . . . . . 2-2

                                                     Page Index-2



 .sixmc . . . . . . . . . . . . . 2-6
 .sixmw . . . . . . . . . . . . . 2-6
 .sixqc . . . . . . . . . . . . . 2-6
 .sixqw . . . . . . . . . . . . . 2-6
 .sixsc . . . . . . . . . . . . . 2-6
 .sixsw . . . . . . . . . . . . . 2-6
 .stopb . . . . . . . . . . . . . 2-13, 8-3
 .t2crl . . . . . . . . . . . . . 2-4
 .t2spc . . . . . . . . . . . . . 2-4
 .t4crl . . . . . . . . . . . . . 2-4
 .t4spc . . . . . . . . . . . . . 2-4
 .tampr . . . . . . . . . . . . . 2-4
 .tapos . . . . . . . . . . . . . 2-4
 .tarow . . . . . . . . . . . . . 2-4
 .tastr . . . . . . . . . . . . . 2-4
 .tatsi . . . . . . . . . . . . . 2-4
 .tbksl . . . . . . . . . . . . . 2-4
 .tblok . . . . . . . . . . . . . 2-3
 .tcart . . . . . . . . . . . . . 2-4
 .tchar . . . . . . . . . . . . . 2-4
 .tcoln . . . . . . . . . . . . . 2-4
 .tcoma . . . . . . . . . . . . . 2-4
 .tcorw . . . . . . . . . . . . . 2-3
 .tcrlf . . . . . . . . . . . . . 2-4
 .tdash . . . . . . . . . . . . . 2-4
 .tdate . . . . . . . . . . . . . 2-3
 .tdatn . . . . . . . . . . . . . 2-3
 .tdec2 . . . . . . . . . . . . . 2-3
 .tdecw . . . . . . . . . . . . . 2-3
 .tdirb . . . . . . . . . . . . . 2-14, D-5
 .tdirb flags . . . . . . . . . . D-5
 .tdolr . . . . . . . . . . . . . 2-4
 .tdttm . . . . . . . . . . . . . 2-3
 .tequl . . . . . . . . . . . . . 2-4
 .texcl . . . . . . . . . . . . . 2-4
 .tfchr . . . . . . . . . . . . . 2-4
 .thash . . . . . . . . . . . . . 2-4
 .tican . . . . . . . . . . . . . 2-9
 .tlang . . . . . . . . . . . . . 2-4
 .tlbrk . . . . . . . . . . . . . 2-4
 .tlpar . . . . . . . . . . . . . 2-4
 .tmohw . . . . . . . . . . . . . 2-2
 .toctw . . . . . . . . . . . . . 2-3
 .toleb . . . . . . . . . . . . . 2-3
 .tpcnt . . . . . . . . . . . . . 2-4
 .tplus . . . . . . . . . . . . . 2-4
 .tppnw . . . . . . . . . . . . . 2-3
 .tquot . . . . . . . . . . . . . 2-4
 .trang . . . . . . . . . . . . . 2-4
 .trbrk . . . . . . . . . . . . . 2-4
 .trdxw . . . . . . . . . . . . . 2-3
 .trpar . . . . . . . . . . . . . 2-4
 .tscan . . . . . . . . . . . . . D-5, H-2
 .tscan flags . . . . . . . . . . D-5

                                                     Page Index-3



 .tsemi . . . . . . . . . . . . . 2-4
 .tsixn . . . . . . . . . . . . . 2-2
 .tslsh . . . . . . . . . . . . . 2-4
 .tspac . . . . . . . . . . . . . 2-4
 .tstrg . . . . . . . . . . . . . 2-2
 .ttabc . . . . . . . . . . . . . 2-4
 .ttime . . . . . . . . . . . . . 2-3
 .ttimn . . . . . . . . . . . . . 2-3
 .tverw . . . . . . . . . . . . . 2-3
 .txwdw . . . . . . . . . . . . . 2-3
 .txwww . . . . . . . . . . . . . 2-2
 .tyoch . . . . . . . . . . . . . 2-1
 .verbo . . . . . . . . . . . . . D-5
 .verbo flags . . . . . . . . . . D-5
 .versc . . . . . . . . . . . . . 2-8
 .versw . . . . . . . . . . . . . 2-8
 .vscan . . . . . . . . . . . . . H-1
 /run switch processing . . . . . 2-11
 ????.l . . . . . . . . . . . . . 5-3
 ????.t . . . . . . . . . . . . . 5-3
 ?????d . . . . . . . . . . . . . 5-4
 ?????l . . . . . . . . . . . . . 5-4
 ?????m . . . . . . . . . . . . . 5-4
 ?????n . . . . . . . . . . . . . 5-4
 ?????p . . . . . . . . . . . . . 5-4
 ????xx . . . . . . . . . . . . . 5-4

 Accumulator names  . . . . . . . E-1
 Acessing scan  . . . . . . . . . 14-1
 Ad.??? . . . . . . . . . . . . . 5-1, 5-3

 Ccl job number . . . . . . . . . 2-11
 Chaining execution . . . . . . . 2-11
 Character checking . . . . . . . 2-9
 Character input  . . . . . . . . 2-9, 2-13
 Character output . . . . . . . . 2-4
 Charater input - positioning . . 2-13
 Clearing input buffers . . . . . 2-13
 Command scanners . . . . . . . . 3-1
 Conversion - scan blocks . . . . 2-13
 Core sizes - inputting . . . . . 2-9
 Core sizes - typing  . . . . . . 2-3
 Credir . . . . . . . . . . . . . 3-2, 13-3, 15-3

 Date conversion routines . . . . 2-11
 Date/time  . . . . . . . . . . . 2-3, 2-6
 Dec date/time - conversion . . . 2-11
 Default values . . . . . . . . . 3-5
 Defaults - absent  . . . . . . . 5-3
 Defaults - present . . . . . . . 5-3
 Defining default values  . . . . 5-1
 Defining keywords for sl switches  5-2
 Defining scanner tables  . . . . 4-1
 Defining switch parameters . . . 4-1

                                                     Page Index-4



 Defining switches  . . . . . . . 3-5
 Defining the storage field . . . 6-1
 Defining values for sl switches  5-1
 Differences - dec/ols  . . . . . C-1
 Dm macro . . . . . . . . . . . . 5-1, 14-1, D-1
 Dm macro definition  . . . . . . D-1
 Doscan macro . . . . . . . . . . 4-1 to 4-2, 5-4, 10-1, 10-4, 
                                  14-1, 15-5, 15-10, A-2, D-2, 
                                  F-3, G-2

 Enter/lookup blocks  . . . . . . 2-14
 Enter/lookup/open blocks - typing  2-3
 Example - credir . . . . . . . . 15-3

 File sizes - inputting . . . . . 2-9
 File sizes - typing  . . . . . . 2-3
 File specification format  . . . 3-4
 File specification input . . . . 2-10
 File specification inputting . . 2-10, 8-1
 File specification output  . . . 2-3
 Fs.??? flags . . . . . . . . . . 4-4, D-3
 Fs.??? symbols . . . . . . . . . D-4
 Fs.icl . . . . . . . . . . . . . 9-3, D-5
 Fs.lrg . . . . . . . . . . . . . 4-5
 Fs.mio . . . . . . . . . . . . . 10-3, D-5
 Fs.mot . . . . . . . . . . . . . 10-3, D-5
 Fs.ncm . . . . . . . . . . . . . 4-5
 Fs.nfs . . . . . . . . . . . . . 4-5
 Fs.nos . . . . . . . . . . . . . 4-5
 Fs.nue . . . . . . . . . . . . . 4-5
 Fs.obv . . . . . . . . . . . . . 4-5
 Fs.vrq . . . . . . . . . . . . . 4-5

 Guide words  . . . . . . . . . . 2-10, 8-2, D-5

 Helper . . . . . . . . . . . . . 10-1, 10-4
 Helper.  . . . . . . . . . . . . 10-4
 Helper.rel . . . . . . . . . . . 14-2

 Initialization . . . . . . . . . 2-1
 Input line positioning . . . . . 2-13
 Input routines . . . . . . . . . 2-6
 Input routines - character . . . 2-13
 Input routines - characters  . . 2-9
 Input routines - clearing input buffers  2-13
 Input routines - core & file sizes  2-9
 Input routines - date/time . . . 2-6
 Input routines - file specifications  2-10
 Input routines - string and numeric  2-6
 Input routines - version numbers  2-8
 Inputting ascii strings  . . . . 2-6
 Inputting core sizes . . . . . . 2-9
 Inputting dates - future . . . . 2-7
 Inputting dates - general  . . . 2-6

                                                     Page Index-5



 Inputting dates - past . . . . . 2-6
 Inputting dates - universal format  2-6
 Inputting decimal numbers  . . . 2-6
 Inputting file sizes . . . . . . 2-9
 Inputting file specifications  . 8-1
 Inputting file specificatons . . 2-10
 Inputting numbers - decimal  . . 2-6
 Inputting numbers - octal  . . . 2-6
 Inputting octal numbers  . . . . 2-6
 Inputting sixbit strings . . . . 2-6
 Inputting sixbit words . . . . . 2-6
 Inputting sixbit words - wild  . 2-6
 Inputting version numbers  . . . 2-8
 Inputting words/strings - ascii  2-6
 Inputting words/strings - sixbit  2-6
 Inputting words/strings - wild sixbit  2-6
 Iscan  . . . . . . . . . . . . . 9-1
 Iscan flags  . . . . . . . . . . D-5

 Jww.cn . . . . . . . . . . . . . D-5
 Jww.fl . . . . . . . . . . . . . D-5
 Jww.pr . . . . . . . . . . . . . D-5

 Keys keys  . . . . . . . . . . . 14-1
 Keys macro . . . . . . . . . . . 5-1 to 5-2, D-2
 Keys macro definition  . . . . . D-2
 Keyword table - address  . . . . 5-3
 Keyword table - entries  . . . . 5-4
 Keyword table - length . . . . . 5-3

 Lookup/enter blocks  . . . . . . 2-14
 Lookup/open blocks - typing  . . 2-3

 Macros - dm  . . . . . . . . . . 5-1, 14-1, D-1
 Macros - doscan  . . . . . . . . 5-4, 10-1, 10-4, 14-1, 15-5, 
                                  15-10, A-2, D-2, F-3, G-2
 Macros - keys  . . . . . . . . . 5-1 to 5-2, 14-1, D-2
 Macros - sl  . . . . . . . . . . 4-3, 6-2, 14-1, D-3
 Macros - sn  . . . . . . . . . . 4-3, 6-2, 14-1, D-3
 Macros - sp  . . . . . . . . . . 4-4, 6-2, 14-1
 Macros - ss  . . . . . . . . . . 4-2, 6-2, 14-1, D-3
 Macros - swtchs  . . . . . . . . D-2
 Manipulating lists of data . . . 2-13
 Masks  . . . . . . . . . . . . . 2-14
 Miscellaneous routines . . . . . 2-11
 Mx.??? . . . . . . . . . . . . . 5-3
 Mx.????  . . . . . . . . . . . . 5-1

 Numeric output . . . . . . . . . 2-3

 Open/lookup blocks - typing  . . 2-3
 Options scanner  . . . . . . . . 11-1
 Oscan  . . . . . . . . . . . . . 3-2, 11-1, H-2
 Output routines - core size  . . 2-3

                                                     Page Index-6



 Output routines - date/time  . . 2-3
 Output routines - file size  . . 2-3
 Output routines - file specifications  2-3
 Output routines - numeric output  2-3
 Output routines - open/lookup block  2-3
 Output routines - ppn  . . . . . 2-3
 Output routines - text . . . . . 2-2

 Partial scanner  . . . . . . . . 13-1
 Pd.??? . . . . . . . . . . . . . 5-3
 Pointr macro . . . . . . . . . . 6-1
 Ppns - typing  . . . . . . . . . 2-3
 Pscan  . . . . . . . . . . . . . 3-2, 13-1, 15-3, H-1

 Qscan  . . . . . . . . . . . . . 13-1, 15-3

 Random number generator  . . . . 2-11
 Register mnemonics . . . . . . . 1-2, E-1
 Register saving  . . . . . . . . 2-2
 Register-saving  . . . . . . . . 2-2
 Run uuo  . . . . . . . . . . . . 2-11

 Scan block conversion  . . . . . 2-13
 Scan blocks  . . . . . . . . . . 2-13 to 2-14, 6-2
 Scan controlling flags . . . . . 4-4
 Scan flags - fs.lrg  . . . . . . 4-5
 Scan flags - fs.ncm  . . . . . . 4-5
 Scan flags - fs.nfs  . . . . . . 4-5
 Scan flags - fs.nos  . . . . . . 4-5
 Scan flags - fs.nue  . . . . . . 4-5
 Scan flags - fs.obv  . . . . . . 4-5
 Scan flags - fs.vrq  . . . . . . 4-5
 Scan switches - sl . . . . . . . 6-2
 Scan switches - sn . . . . . . . 6-2
 Scan switches - sp . . . . . . . 6-2
 Scan switches - ss . . . . . . . 6-2
 Scnmac . . . . . . . . . . . . . D-1
 Sixbit masks . . . . . . . . . . 2-14
 Sl . . . . . . . . . . . . . . . 14-1
 Sl macro . . . . . . . . . . . . 4-3, 6-2, D-3
 Sl macro definition  . . . . . . D-3
 Sn . . . . . . . . . . . . . . . 14-1
 Sn macro . . . . . . . . . . . . 4-3, 6-2, D-3
 Sn macro definition  . . . . . . D-3
 Sp . . . . . . . . . . . . . . . 14-1
 Sp macro . . . . . . . . . . . . 4-4, 6-2
 Space allocation . . . . . . . . 2-2
 Ss . . . . . . . . . . . . . . . 14-1
 Ss macro . . . . . . . . . . . . 4-2, 6-2, D-3
 Ss macro definition  . . . . . . D-3
 Storage field - file specification  6-2
 Suffixes - decimal & octal input  2-6
 Switch formats . . . . . . . . . 3-3
 Switch tables - defaults . . . . 5-4

                                                     Page Index-7



 Switch tables - length . . . . . 5-4
 Switch tables - names  . . . . . 5-4
 Switch tables - processors . . . 5-4
 Switch tables - storage  . . . . 5-4
 Switch types - sl  . . . . . . . 4-3
 Switch types - sn  . . . . . . . 4-3
 Switch types - sp  . . . . . . . 4-4
 Switch types - ss  . . . . . . . 4-2
 Swtchs macro . . . . . . . . . . 3-5, D-2
 Swtchs macro - definition  . . . 4-2
 Swtchs macro - usage . . . . . . 4-1
 Swtchs macro definition  . . . . D-2

 Table searching  . . . . . . . . 2-11
 Testing for logged-in jobs . . . 2-14
 Traditional scanner  . . . . . . 10-1
 Ts.drb . . . . . . . . . . . . . D-5
 Ts.drp . . . . . . . . . . . . . D-5
 Ts.drw . . . . . . . . . . . . . D-5
 Tscan  . . . . . . . . . . . . . 3-1, 10-1, H-2
 Tscan flags  . . . . . . . . . . D-5
 Typing directory information . . 2-14
 Typing lookup/enter blocks . . . 2-14
 Typing open/lookup blocks  . . . 2-3
 Typing path blocks . . . . . . . 2-14
 Typing ppns  . . . . . . . . . . 2-3
 Typing scan blocks . . . . . . . 2-14

 Universal date/time - conversion  2-11
 Universal date/time - current  . 2-11
 Unversal date/time input . . . . 2-6
 Using the miscellaneous routines  2-11, 2-13 to 2-14
 Using the miscellaneous routines.  2-11, 2-14
 Using wild . . . . . . . . . . . B-1

 Verb form scanner  . . . . . . . 12-1
 Version numbers - inputting  . . 2-8
 Version numbers - typing . . . . 2-3
 Vscan  . . . . . . . . . . . . . 3-2, 12-1, H-1

 Wild . . . . . . . . . . . . . . 8-2 to 8-3, 8-5