Table of Contents
                                                                     page
               1.0 INTRODUCTION                                       2
               2.0 TYPOGRAPHICAL CONVENTIONS                          2
               3.0 RUNNING BIBLIO                                     3
               4.0 COMMANDS                                           3
                   4.1  The H (Help) Command                          3
                   4.2  The E (Exit) Command                          4
                   4.3  The N (Name) Command                          4
                   4.4  The I (Insert) Command                        4
                   4.5  The A (Append) Command                        5
                   4.6  The T (Type) Command                          6
                   4.7  The P (Page) Command                          6
                   4.8  The B (Begin) Command                         7
                   4.9  The F (Find) Command                          7
                   4.10 The S (Search) Command                        9
                   4.11 The D (Dump) Command                          10
                   4.12 The K (Kill) Command                          10
                   4.13 The R (Replace) Command                       10
               5.0 ADVANCED EDITING                                   12
                   5.1 Internal format of BIBLIO data files           12
                   5.2 Editing Precautions                            13

     User Guide to BIBLIO                                            Page 2
               BIBLIO.DOC(2.0)[21-JUN-79]/MDR
                              User Guide to BIBLIO
                                 (VERSION 2.0)
               1.0  INTRODUCTION
               BIBLIO is a program which creates  and/or  searches  through
               bibliographical  references  in a data file on the computer.
               Its capabilities include:
                 - Creating a data file
                 - Appending bibliographical references to an old data file
                 - Finding the next match of a search string in a data file
                 - Finding all matches of a search string in a data file
                 - Editing the data file
               BIBLIO was written by Mike Rubin of the  Wesleyan  Computing
               Center in June, 1979.
               2.0  TYPOGRAPHICAL CONVENTIONS
               The (CR) notation represents the carriage return key (RETURN
               or NEW LINE) on the terminal keyboard.
               The notation CTRL-<character> represents a control character

     User Guide to BIBLIO                                            Page 3
               typed  by  holding  down  the  CONTROL  or  CTRL  key on the
               terminal keyboard and typing the character.
               3.0  RUNNING BIBLIO
                    To run BIBLIO,  type  .RUN  BIBLIO(CR) .   BIBLIO  will
                                          _
               respond with:
                    Data file name:
                    The user should type in the name of the  data  file  he
               wishes to create and/or use followed by a (CR).
                    BIBLIO will then ask for a command, and the user should
               type in one of the commands listed below.
               4.0  COMMANDS
               4.1  The H (Help) Command
               The form of the Help command is:
                    H(CR)
               This command will type out a short help text on the terminal
               and then return to BIBLIO command mode.

     User Guide to BIBLIO                                            Page 4
               4.2  The E (Exit) Command
               The form of the Exit command is:
                    E(CR)
               This command will return the user to monitor  command  mode.
               The  user  may  also type CTRL-C at any time to exit BIBLIO.
               If CTRL-C is typed while the user  is  inserting  an  entry,
               that entry will not be inserted in the data file.
               4.3  The N (Name) Command
               The form of the Name command is:
                    N(CR)
               This command will prompt BIBLIO to again ask for a data file
               name, and subsequent commands will apply to the file named.
               4.4  The I (Insert) Command
               The form of the Insert command is:
                    I(CR)
               This command has two purposes.
               1. If the data file named does not exist, the Insert command
               will create the file and insert the first entry into it.

     User Guide to BIBLIO                                            Page 5
               2. If the data file named does  exist,  the  Insert  command
               will  insert  a  new  entry  before  the current entry.  The
               current entry is defined as  the  entry  last  displayed  or
               edited.
               This command will clear the screen and ask for text to  fill
               each of four fields: (1)title, (2)author, (3)publication and
               page references, and (4)summary/abstract.
               The information placed in each field consists of one or more
               lines  of  characters  terminated  by  a  CTRL-Z.  After all
               fields have been filled, BIBLIO will return to command mode.
               It  is  not  necessary to type (CR) after the last line of a
               field has been inserted.
               4.5  The A (Append) Command
               The form of the Append command is:
                    A(CR)
               This command will prompt BIBLIO to ask the  same  series  of
               questions  as for the Insert command.  (See section 4.4.) It
               will append this new entry to the end of the data file.

     User Guide to BIBLIO                                            Page 6
               4.6  The T (Type) Command
               The form of the Type command is:
                    T(CR)
               This  command  will  type  out  the  current  entry  on  the
               terminal.
               4.7  The P (Page) Command
               The form of the Page command is:
                    P(CR)
               This command will type out the next entry, i.e.,  the  entry
               following  the  current  entry,  on  the  terminal.   Typing
               successive Page commands will page through the file.
               4.8  The B (Begin) Command
               The form of the Begin command is:
                    B(CR)
               This command defines the current entry as the first entry in
               the data file.

     User Guide to BIBLIO                                            Page 7
               4.9  The F (Find) Command
               The form of the Find command is:
                    F[<fields to search>][:<search string>](CR)
                    where <search string>  can  be  any  series  of  words,
               square brackets [] indicate an optional part of the command,
               and <fields to search> can be one or more of  the  following
               codes:
                    A   Author fields
                    R   Reference fields
                    S   Summary/abstract fields
                    T   Title fields
               If no field codes are given, all fields  will  be  searched.
               This  command will find the first match of the search string
               in the data file and type out the entry in which  the  match
               was  made  on  the  terminal.   A  match  is  defined as the
               presence of every word in the search  string  in  any  order
               within  a  single  field.   The upper and lower cases of the
               same letter are treated as the same character.  To find  the
               next match of the search string, type:
                    F(CR)

     User Guide to BIBLIO                                            Page 8
               For example:
             Command: F:FORTRAN programming(CR)   Find the first  match  of
             ________
                                                  "FORTRAN    programming,"
                                                  and  type  the  entry  in
                                                  which  the match was made
                                                  on the terminal.
             Command: F(CR)                       Find the  next  match  of
             ________
                                                  "FORTRAN    programming,"
                                                  and  type  the  entry  in
                                                  which  the match was made
                                                  on the terminal.
             Command: FTS(CR)                     Search in just the  Title
             ________
                                                  and  Summary  /  abstract
                                                  fields for the next match
                                                  of "FORTRAN programming."
             Command: FA:PASCAL(CR)               Find the first  match  of
             ________
                                                  "PASCAL"   in  an  Author
                                                  field.
             COMMAND: F(CR)                       Find the  next  match  of
             ________
                                                  "PASCAL"   in  an  Author
                                                  field.

     User Guide to BIBLIO                                            Page 9
               4.10  The S (Search) Command
               The basic form of the Search command is:
                    S[<fields to search>][:<search string>](CR)
               This command will write all entries  containing  matches  of
               the  search  string  to  a  file  whose  name is of the form
               Q??.LPT, where the question marks  will  be  letters  and/or
               numbers.   Field codes may be given with the Search commands
               as for the Find command.  (See section 4.9.)
               If no search string is given, and if the last command was  a
               successful  Find  command  (i.e.,  The match was made.), the
               Search command will use the same search string that the Find
               command used.
               For example:
             Command: F:ALGOL                     Find the first  match  of
             ________
                                                  "ALGOL," and type out the
                                                  entry in which it  occurs
                                                  on the terminal.
             Command: SST                         Search for all matches of
             ________
                                                  "ALGOL" in just Title and
                                                  Summary field, and  write
                                                  all   entries   in  which
                                                  matches  are  made  to  a
                                                  file of the form Q??.LPT.

     User Guide to BIBLIO                                           Page 10
               4.11  The D (Dump) Command
               The form of the Dump command is:
                    D(CR)
               This  command  will  create  a  file  of  the  form  Q??.LPT
               consisting  of a complete listing in report form of the data
               file.
               4.12  The K (Kill) Command
               The form of the Kill command is:
                    K(CR)
               This command will delete the current entry.
               4.13  The R (Replace) Command
               The form of the Replace command is:
                    R[<list of fields to replace>](CR)
               This command  will  replace  fields  in  the  current  entry
               specified  by the field codes.  The field codes are the same
               as for the Find and Search commands.  (See sections 4.9  and
               4.10.)  BIBLIO  prompts for each field as for the Insert and
               Append commands.  (See sections 4.4 and 4.5.)  If  no  field

     User Guide to BIBLIO                                           Page 11
               codes are given, all fields will be replaced.
               For example:
             Command:RAT(CR)                      Replace  the  Author  and
             ________
                                                  Title   fields   in   the
                                                  current entry.
             Command:R(CR)                        Replace the current entry
             ________
                                                  in its entirety.

     User Guide to BIBLIO                                           Page 12
               5.0  ADVANCED EDITING
               This section requires knowledge of one of the  text  editors
               on  your  computer.   If  the  user  wishes to edit his data
               file(s), he should familiarize himself  with  one  of  these
               editors before continuing.
               5.1  Internal Format Of BIBLIO Data Files
               The data file is divided into pages terminated by formfeeds.
               Each  page  contains one bibliographical entry consisting of
               four fields.  Each field begins with a decimal  point.   The
               decimal  point  is followed by the code for the field.  (See
               section 4.9.) This code preceeds a  colon  which,  in  turn,
               preceeds the field string.
               e.g., .A:John Smith
                     Harry Jones
                     .T:A User's Guide
                     .R:Wesleyan University Press
                     Pages 100-567
                     .S:Tells the user how, why, what, and where to do it.
                     Includes a special appendix suggesting with whom to do
                     it.
                     Keys = instructional, vague
                     (formfeed)

     User Guide to BIBLIO                                           Page 13
               5.2  Editing Precautions
               The user may edit a BIBLIO data file with any editor, but he
               must take the following precautions:
                  1. If using a line-oriented editor, line-numbers must  be
                  stripped before exiting.
                  2. Page-marks (formfeeds) must  not  be  stripped  except
                  when  an  entire  page is deleted.  In this special case,
                  the page mark at the end of the deleted page must also be
                  deleted.
                  3. Data files should  be  printed  only  when  absolutely
                  necessary  to avoid wasting paper as a result of the many
                  form feeds in the file.  If the user wants a  listing  of
                  all  entries in the file, he should use the Dump command.
                  (See section 4.11.)
                  4. A file whose extension is .DAT must  be  printed  with
                  the following command string:
                       .PRINT <filename>.DAT/FILE:ASCII(CR)
                       _
                  to avoid carriage-control functions.

     User Guide to BIBLIO                                           Page 14
                           Summary of BIBLIO Commands
     A                                            Append an  entry  to  the
                                                  data file
     B                                            Position at Beginning  of
                                                  data file
     D                                            Dump  all  entries  to  a
                                                  disk file
     E                                            Exit
     F[<list of field codes>][:<search string>]   Find the next  match  and
                                                  type out the entry on the
                                                  terminal
     H                                            Type this  Help  text  on
                                                  the terminal
     I                                            Insert a new entry before
                                                  the current entry
     K                                            Kill the current entry
     N                                            Name  a  different   data
                                                  file
     P                                            Page to next entry
     R[<list of field codes>]                     Replace  fields  in   the
                                                  current entry
     S[<list of field codes>][:<search string>]   Search for all matches in
                                                  the  data  file and write
                                                  entries to a disk file
     T                                            Type the current entry on
                                                  the terminal
     Optional field codes are:
          A                                       Author fields
          T                                       Title fields
          R                                       Reference fields
          S                                       Summary fields