PDP-8 SIMULATOR
			===============
				--------
				ABSTRACT
			         ========

		THE PDP-8 SIMULATOR HAS TWO MAIN PARTS, THE 

	FIRST ACCEPTS INPUT IN PAL III LANGUAGE AND ASSEMBLES IT, AND

	THE SECOND EXECUTES THE INPUT PROGRAM.

		AT EACH STAGE OF OPERATION, INPUT, ASSEMBLY OR EXECUTION

	THE SIMULATED PDP-8 MEMORY CAN BE EXAMINED, IN OCTAL DIGITS.

		THE SIMULATOR ASSEMBLES AND EXECUTES MANY OF THE PAL III

	INSTRUCTIONS, BUT ONLY A PORTION OF THE INPUT-OUTPUT INSTRUCTIONS,

	AND NONE OF THE MICROPROGRAMMING FACILITIES ARE AVAILABLE.

		COMMUNICATION AND INTERACTION WITH THE SIMULATOR ARE DONE

	THROUGH THE TELETYPE , WHICH IS ALSO THE ONLY PERIPHERAL DEVICE

	HANDLED BY THE SIMULATOR.

		PROGRAMS CAN BE STORED AND RECALLED USING THE

	DISK OPERATIONS FACILITIES.

		THIS PROGRAM WAS WRITTEN IN MACRO-10 ON THE BRANDEIS

	UNIVERSITY PDP-10 COMPUTER.  WE WISH TO THANK THE COMPUTER STAFF

	AND PROFFESOR MAX CHRETIEN FOR THEIR COOPERATION.
	







	DESCRIPTION, PRINCIPLES OF OPERATION AND GENERAL FEATURES OF

			PDP-8 SIMULATOR,

	MACRO-10 PROGRAM, WRITTEN ON BRANDEIS' PDP-10 COMPUTER BY











		ODED SHMUELI    '77

		KWABENA AKUFO   '77







			ADVISOR:  MAX CHRETIEN
				   PROF. OF PHYSICS
				   BRANDEIS UNIVERSITY

			   DATE: OCTOBER 1975































		C O N T E N T S
		= = = = = = = =

	1.  BASIC PRINCIPLES

	2.  USERS' VIEW (SIMPLIFIED)

	3.  GENERAL FEATURES

	4.  CONCLUSION


	APPENDIX A.   SAMPLE PROGRAM IN PAL III

	APPENDIX B.   GENERAL FLOWCHART

	APPENDIX C.   PROCEDURAL USE OF SIMULATOR INCLUDING

		      (I) PROGRAM INPUT

		      (II) EXAMINATION OF LOCATIONS

		    (III)   WRITING ON, AND READING FROM DISK

		    (IV)   EXECUTION AND EXAMINATION OF RESULTS

		    (V)   MODIFICATION OF PROGRAM

		    (VI)   READING OF A STORED PROGRAM FROM DISK,
				EXECUTING IT.

	APPENDIX D.   AVAILABLE INSTRUCTIONS

	APPENDIX E.   PROGRAM LISTING OF THE PDP-8 SIMULATOR




















		BASIC PRINCIPLES


		THE PROGRAM IS MADE UP OF TWO MAIN PARTS.  THE FIRST

	PART CONSISTS OF AN INPUT UNIT FOR PAL III PROGRAMS AND AN

	ASSEMBLER.  THE OUTPUT OF THE ASSEMBLER IS IDENTICAL TO

	THAT OF THE PDP-8 ASSEMBLER, AND IS STORED IN AN ARRAY

	CALLED PDP-8.

		THE SECOND PART OF THE PROGRAM, WHICH IS INDEPENDENT

	OF THE FIRST, SIMULATES THE ACTUAL EXECUTION OF A PALL III

	PROGRAM ON THE PDP-8.  THIS PART CAN HANDLE MEMORY REFERENCE

	INSTRUCTIONS, OPERATE MICROINSTRUCTIONS, AND INPUT/OUTPUT
			      1
	TRANSFER INSTRUCTIONS.   MICROPROGRAMMING AND AUTOINDEXING

	FACILITIES ARE NOT AVAILABLE.  SINCE THE TELETYPE IS THE

	ONLY MEDIUM OF COMMUNICATION BETWEEN THE USER AND THE

	SIMULATOR, THE INTERRUPT FACILITY OF THE PDP-8 IS NOT NEEDED

	AND THEREFORE NOT SIMULATED EXCEPT FOR THE TELETYPE, WHICH IS

	AN ACTUAL MEDIUM OF COMMUNICATION.


			USERS'  VIEW

		A GOOD WAY TO DESCRIBE THE USE OF THIS SIMULATOR IS

	THROUGH THE USE OF ILLUSTRATIONS FOLLOWED BY A GENERAL

	DISCUSSION.

	PROBLEM: WRITE A PROGRAM TO SUM THE NUMBERS 2,-3,10
		REFER APPENDIX A FOR SAMPLE PROGRAM.

	1.
	  REFER TO APPENDIX D FOR LIST OF INSTRUCTIONS AVAILABLE ON
	  THE SIMULATOR.








			-2-





	STEP 1.
		IN THE MONITOR MODE TYPE

	.EX PDP/M,TR.MAC

	STEP 2.
		THE USER WILL RECEIVE THE FOLLOWING MESSAGES AT THE

	START OF THE EXECTION OF THE SIMULATOR PROGRAM:


	.EX PDP/M.TR.MAC
	LINK:   LOADING
	[LNKXCT PDP EXECUTION]
	TYPE 1,2,3,4,5,6,7,A,B,C,D
	B: COMPILE, C OR D: EXECUTE, 3: COPY FROM DISK, 6: WRITE N DISK
	4: TO START WRITING PROGRAM WITH * (DESTROYS OTHER PROGRAMS ON FILE)
	5: START PROGRAM INPUT (PRESERVES OTHER PROGRAMS ON FILE
	UPPER CASE 1(!): INTERRUPT FACILITY TO EXAMINE COMPILATION ANYWHERE
	CENT

		FOLLOWING THE WORD 'CENT' AT THE END OF THE ABOVE

	MESSAGES, TYPE '4'.

		ADDITIONAL MESSAGES WILL BE OUTPUT.

	4INITIALIZATION WILL BE DONE NOW
	PD8 TABLE NUMBERED
	INPUT PROGRAM


		AFTER THE MESSAGE 'INPUT PROGRAM', THE USER SHOULD

	TYPE AN ASTERISK(*) AND WAIT FOR THE OUTPUT OF A BLANK. 

	THEN TYPE THE STARTING LOCATION OF THE PROGRAM AND 

	RETURN THE CARRIAGE.

		THE USER GETS THE MESSAGE

	* 200
	LC VALUE (*) KNOWN IS IN LC
















			THE USER WILL THEN START INPUT OF THE PROGRAM IN THE FOLLOWING WAY:
		(1) LABELS,IF THEY EXIST SHOULD ALWAYS CONSIST OF TWO
		CHARACTERS.IF THE LINE CONTAINS NO LABEL , CONTROL I
		SHOULD BE TYPED. IN EITHER CASE , THE USER SHOULD WAIT UNTIL BLANKS
		ARE OUTPUT AND THEN RESUME INPUT BY TYPING EITHER A COLON(:) OR COMMA(,).

			COLON(:)INDICATES THAT WHAT FOLLOWS IS A MNEMONICS.
			COMMA(,)INDICATES A NUMBER TO FOLLOW.




		(2) MNEMONICS SHOULD BE A VALID PAL III INSTRUCTION ,
		OTHERWISE THE USER WILL RECEIVE AN ERROR MESSAGE AND WILL BE
		ENCOURAGED TO TRY AGAIN.




		(3) INDIRECT ADRESSING IS DONE BY TYPING 'I' AFTER
		THE MNEMONICS.




		(4) IF THERE IS AN OPERAND IT MUST BE TWO CHARACTERS
		LONG. AT THE END OF INPUT OF THE OPERAND THE TELETYPE WILL
		AUTOMATICALLY MOVE TO TO THE NEXT LINE TO ACCEPT FURTHER INPUT.
		IN CASE THERE IS NO OPERAND , THE USER SHOULD TYPE A CARRIAGE RETURN.






		NUMBERS ARE OCTAL AND SHOULD BE PRECEDED WITH EITHER A PLUS
		OR A MINUS SIGN. IN THE CASE OF A MINUS , THE SIMULATOR
		ACKNOWLEDGES RECEIPT BY OUTPUTTING "(MINUS)". AFTER A NUMBER ,
		THE USER SHOULD FIRST TYPE ONE CARRIAGE RETURN TO INDICATE
		THE END OF INPUT OF THE NUMBER AND THEN TYPE A SECOND ONE TO
		RETURN TO THE NEXT LINE.


		(NOTE: ZERO MUST BE PRECEDED BY A PLUS SIGN.)





			-3-





		COMPILATION OF PROGRAM STARTS BY TYPING UPPERCASE P(@) AT THE

	BEGINING OF A NEW LINE.  THE USER RECEIVES THE FOLLOWING MESSAGE:

			: DCA
			: HLT
	CC	,+43
	D5	,-(MINUS)21
	@
	COMPILATION STARTS

	!!! TO INTERRUPT, ANYTHING TO CONTINUE


		IF THE USER TYPES ANYTHING OTHER THAN UPPERCASE 1(!),

	THE USER GETS TO 'CENT'.(THE PROGRAM CONTROL CENTER)

		TO EXECUTE, THE USER SHOULD TYPE 'C'.

	THE SIMULATOR RESPONDS IN THE FOLLOWING MANNER:

				,CENT

	CSTART EXEC. AT LABEL:


		THE USER HAS TO SUPPLY A LABEL WHICH SHOWS WHERE

	EXECUTION IS TO BEGIN.


	!!! TO INTERRUPT, ANYTHING TO CONTINUE/CENT
	CSTART EXEC. AT LABEL: KK

	AC AT END OF EXECUTION: 000000000000
	! TO DEBUG ANYTHING TO CONTINUE


		DEBUGGING FACILITIES ENABLE USER TO EXAMINE

	LOCATIONS IN THE SIMULATED PDP-8.  AFTER EXECUTION, SHOULD THE

	USER TYPE UPPERCASE 1(!) THE SIMULATOR RESPONDS AS

	FOLLOWS:


					!!!!!...INTERUPTION...!!!
	INPUT LOW LC TO TRANSLATE

	400




				-5-



		THE USER SHOULD TYPE THE OCTAL VALUE OF THE

	LOCATION, AT WHICH EXAMINATION IS TO BEGIN, IN THE PDP-8

	THE SIMULATOR RESPONDS BY TYPING:


	UP LC TO TRANS.

	400


		USER SHOULD TYPE THE OCTAL VALUE OF THE LOCATION UP

	TO WHEREVER EXAMINATION IS TO BE DONE.

		THE COMPUTER WILL THEN GIVE AN OCTAL LISTING OF

	THOSE LOCATIONS AND THEIR CONTENTS. (SEE APPENDIX C)

	TO COME BACK TO CENT.  TYPE UPPERCASE L(\)



































				-6-



			GENERAL FEATURES


		LOOKING AT APPENDIX B, ONE WILL NOTICE THE DISK

	OPERATIONS AND THE VARIETY OF POSSIBILITIES IN INPUT,

	EXAMINATION, EXECUTION AND DEBUGGING OF A PROGRAM.  WE

	SHALL DISCUSS CERTAIN IMPORTANT PROCEDURES.

	THE USE OF STATE S1 AND S3

		THE '4', SHOULD NOT BE IN MOST CASES TYPED

	TWICE (AT CENT), SINCE ONE FEATURE OF STATE S1 IS TO ZERO

	THE WHOLE SIMULATED PDP-8 MEMORY.  THUS SHOULD THE USER

	WISH TO RETURN TO INPUT MODE, STATE S3, TO INPUT NEW PROGRAMS

	OR TO CHANGE EXISTING ONES, A '5' SHOULD BE TYPED (AT CENT)

	INSTEAD OF '4'.

		IN GENERAL, '4' IS TYPED ONLY ONCE AT THE VERY

	BEGINING OF THE USE OF THE SIMULATOR, AND AFTERWARDS '5' IS

	USED TO RESUME INPUT.

	READING AND WRITING ON DISK FILES

		THE USER SHOULD NOTE THE FOLLOWING:

		WHENEVER THE USER WRITES ONTO THE DISK FILE TO STORE

	A PROGRAM, WHATEVER IS ON THE DISK FILE, IS REPLACED BY

	THE WHOLE OF THE CURRENT SIMULATED PDP-8 MEMORY.

		SIMILARLY, READING STORED PROGRAMS FROM DISK FILE

	REPLACES ALL OF THE CURRENT SIMULATED PDP-8 MEMORY BY

	WHATEVER IS ON THE DISK FILE.

		THUS, IF THERE IS A PROGRAM ON THE DISK FILE WHICH THE

	USER WISHES TO USE WITH OTHER PROGRAMS THAT ARE YET TO 

	BE INPUT, THE USER SHOULD EMPLOY THE FOLLOWING PROCEDURE,





				-7-




		(A)  COPY FROM DISK

		(B)  TYPE THE NEW PROGRAMS OR MAKE CORRECTIONS TO

		     THE PREVIOUSLY DISK STORED PROGRAM.

	DEBUGGING
	=========

		THE USER SHOULD BE AWARE THAT ONCE COMPILATION IS

	DONE, THE MNEMONIC SOURCE PROGRAM IS NO LONGER STORED.

	THUS DEBUGGING IS DONE IN CLOSE CONNECTION WITH THE PDP-8

	MACHINE LANGUAGE.  USING UPPERCASE 1(!), THE USER CAN EXAMINE

	ANY LOCATION IN THE SIMULATED PDP-8 MEMORY.

		EXAMPLES ARE PROVIDED IN APPENDIX C.

	CORRECTIONS TO PROGRAM
	======================

		SHOULD A NEED TO MAKE CORRECTIONS IN A PROGRAM ARISE,

	THE USER TYPE '5' AT CENT.

		AFTER RECEIVING THE MESSAGE, 'INPUT PROGRAM', THE

	USER SHOULD TYPE * (LOCATION NUMBER) TO RECEIVE;

		LC VALUE (*) KNOWN IS IN LC

	THEN THE LOCATION CAN BE REPLACED SIMPLY BY TYPING THE NEW LINE.

		REPLACEMENTS CAN BE DONE FOR ANY OTHER LOCATIO WITH

	NO NEED TO GO BACK TO CENT.




		CONSULT APPENDIX C FOR FURTHER DETAILS AND EXAMPES











				-8-


			CONCLUSION


		A FINAL REMARK CONCERNS THE REACTION TIME OF THE

	TELETYPE.  WHEN THE COMPUTER IS VERY BUSY, THE USER ADVISED TO TYPE

	THE PROGRAM VERY SLOWLY AND ALWAYS TO USE A RELIABLE TELETYPE.

	THE USE OF THE PRINTING TELETYPE IS PREFERRED TO THAT

	OF THE CRT TELETYPE.

		THE MOST IMPORTANT PART OF THIS PAPER IS APPENDIX B

	AND THE USER IS ADVISED TO HAVE A COPY OF IT CLOSE BY 

	WHILE USING THE SIMULATOR PROGRAM.  WE ARE AWARE THAT USERS MIGHT

	FIND IT DIFFICULT TO ADJUST TO A SYSTEM THAT HAS MNEMONICS INPUT

	FACILITIES, MACHINE LANGUAGE DEBUGGING FACILITIES AND IN

	WHICH COMPILING, LOADING, DEBUGGING AND EXECUTION ARE BASICALLY

	DONE CONTINUOUSLY AND AT ANY DESIRED SEQUENCE.

	NEVERTHELESS, WE FEEL IT IS A GOOD INTRODUCTION TO 

	BOTH MACHINE LANGUAGE AND SYSTEM PROGRAMMING.

		THROUGH THIS PROJECT WE HAVE GAINED A NEW INSIGHT

	INTO SOFTWARE DESIGN PROBLEMS, HOWEVER PRIMITIVE AND LIMITED

	THE OPERATING SYSTEM THAT WE HAVE CREATED IS.
























CIRCLE	: A CHARACTER TO TYPE WHEN IN CENT.

ELIPSE	: A CHARACTER TO TYPE TO SWITCH STATES



S                S  : BY TYPING C YOU GET FROM 
		          STATE S   TO STATE  S


   		: INDICATES AUTOMATIC TRANSITION AFTER COMPLETION OF MISSION.


CENT: ANY TYPING IN THE 'CENT' STATE SHOULD BE DONE 
	FOLLOWING THE OUTPUT OF THE WORD 'CENT'.

  ! : IN CENT, S3 :TYPING UILL PRODUCE TRANSLATION 
MESSAGES BEGINING "LOW LC TO TRANSLATE".

	AT ALL OTHER STATES UPPERCASE 1(!) SHOULD BE TYPED ONLY WHEN
	MESQAGE GIVES THE USER OPTION TO DO SO.









		APPENDIX D


	THE FOLLOWING ARE PAL III INSTRUCTIONS THAT CAN BE USED
ON THE SIMULATOR.

	MEMORY REFERENCE INSTRUCTIONS

	AND
	TAD
	ISZ
	DCA
	JMS
	JMP	(JMP .-1 NOT ALLOWED)


	GROUP 1 OPERATE MICROINSTRUCTIONS

	NOP
	CLA
	CLL
	CMA
	CML
	RAR
	RAL
	RTR
	RTL
	IAC


	GROUP 2 OPERATE MICROINSTRUCTIONS

	SMA
	SZA
	SPA
	SNA
	SNL
	SZL
	SKP
	HLT


	TELETYPE KEYBOARD READER

	KCF
	KSF
	KCA
	KRS
	KRB


	TELETYPE TELEPRINTER

	TFL
	TSF
	TCF
	TPC
	TLS






00020			APPENDIX C
00040	
00060	
00080	
00100	* 200
00200	LC VALUE (*) KNOWN IS IN LC
00300	
00400	ST	: CLA
00500			: CLL
00580			: TAD RQ
00590			: DCA RG
00600			: TLS
00700			: TAD MC
00800			: DCA CT
00900	NX	: TAD I RG
01000			: JMS TY
01100			: ISZ RG
01200			: ISZ CT
01300			: JMP NX
01400			: HLT
01500	TY	,+0
01600	T2	: TSF
01700			: JMP T2
01800			: TLS
01900			: CLA
02000			: JMP I TY
02100	MC	,-(MINUS)15
02200	CT	,+0
02300	RG	,+0
02350	RQ	,+400
02400	*400
02500	LC VALUE (*) KNOWN IS IN LC
02600	
02700	JJ	,+312
02800	OO	,+317
02900	HH	,+310
03000	N1	,+316
03100	B1	,+240
03200	A1	,+301
03300	N2	,+316
03400	DD	,+304
03500	B2	,+240
03600	MM	,+315
03700	A2	,+301
03800	RR	,+322
03900	YY	,+331
04000	@
04100	COMPILATION STARTS 
04200	
04300	!!! TO INTERRUPT, ANYTHING TO CONTINUE/CENT
04400	CSTART EXEC. AT LABEL: ST
04500	
04550	JOHN AND MARY
04600	AC AT END OF EXECUTION : 000000000000
04700	!  TO DEBUG ANYTHING TO CONTINUE/END OF DEBUG
05000	UPPER CASE L(\) TO EXIT ANYTHING TO DEBUG AGAIN
05100	\CENT
05300	5INPUT PROGRAM
05400	* 221
05600	LC VALUE (*) KNOWN IS IN LC
05700	
05800	MC	,-(MINUS)14
05900	*411
05980	LC VALUE (*) KNOWN IS IN LC
05990	
06000	SS	,+323
06100	UU	,+325
06200	EE	,+305
06300	@
06400	COMPILATION STARTS 
06500	
06600	!!! TO INTERRUPT, ANYTHING TO CONTINUE!!!!...INTERUPTION...!!!
06700	INPUT LOW LC TO TRANSLATE
06800	
06900	221
07100	UP LC TO TRANS.
07200	
07300	221
07400	
07500		000000000221     777777777764
07600	
07650	CENT
07700	!!!!...INTERUPTION...!!!
07800	INPUT LOW LC TO TRANSLATE
07900	
08000	411
08200	UP LC TO TRANS.
08300	
08400	413
08500	
08600		000000000411     000000000323
08650	
08700		000000000412     000000000325
08750	
08800		000000000413     000000000305
08850	
08900	CENT
09000	CSTART EXEC. AT LABEL: ST
09100	
09200	JOHN AND SUE
09300	
09400	AC AT END OF EXECUTION: 000000000000
09500	!  TO DEBUG ANYTHING TO CONTINUEH END OF DEBUG
09600	UPPERCASE L(\) TO EXIT, ANYTHING TO DEBUG AGAIN\
09700	CENT
00100			APPENDIX A
00200	
00300	
00400	
00500	* 200
00600	LC VALUE (*) KNOWN IS IN LC
00700	
00800	BG	: CLA
00900			: CLL
01000			: TAD N1
01100			: TAD N2
01200			: TAD N3
01300			: DCA SM
01400			: HLT
01500	N1	,+2
01600	N2	,-(MINUS)3
01700	N3	,+10
01800	SM	,+0
01900	@
02000	COMPILATION STARTS
02100	
02200	!!! TO INTERUPT, ANYTHING TO CONTINUE/CENT
02300	6CENT
02400	CSTART EXEC. AT LABEL: BG
02500	
02600	AC AT END OF EXECUTION: 000000000000
02700	!  TO DEBUG ANYTHING TO CONTINUE!!!!...INTERUPTION...!!!
02800	INPUT LOW LC TO TRANSLATE
02900	
03000	212
03100	UP LC TO TRANS.
03200	
03300	212
03400	
03500		000000000212     000000000007
03600	
03700	END OF DEBUG
03800	UPPERCASE L(\) TO EXIT, ANYTHING TO DEBUG AGAIN
03900	\CENT




					BOX 1537,
					BRANDEIS UNIVERSITY,
					WALTHAM, MASS. 02154
					OCT. 24, 1975


DEAR SIRS,
	  ENCLOSED IS A PAPER DESCRIBING THE FEATURES OF
A PDP-8 SIMULATOR.

	 PLEASE, LET US KNOW WHETHER YOU ARE INTERESTED IN
THIS SIMULATOR PROGRAM.

				SINCERELY YOURS

					ODED SHMUELI
					KWABENA AKUFO


DIGITAL EQUIPMENT CORPORATION
SOFTWARE DEPARTMENT
MAYNARD,MASSACHUSETTS 01754