1.0  PURPOSE

          PENNZYME  is  a  program  for  fitting  trial  rate  laws   to
     experimental  data  from steady state initial velocity experiments.
     It determines the set of parameter values  for  a  given  rate  law
     which  produces  the  closest  fit  to  the  experimental data, and
     provides information as to how good that fit is.



     2.0  ABSTRACT

          This program finds the set  of  parameter  values  in  a  user
     supplied  rate law which gives the best fit to the initial velocity
     data.   The  program  operates  interactively  and   provides   two
     algorithms  for  locating  a  least-squares fit to the experimental
     data.  The algorithms have different convergence properties and are
     best applied independently or in sequence with independent stopping
     criteria.  The two algorithms were selected  to  work  together  so
     their capabilities complement each other.

          The program allows the user to interactively alter the initial
     parameter  values, which parameters are actually being varied in an
     optimization, the stopping criteria, the order  of  application  of
     the  fitting algorithms, and to delete points which the program has
     identified as outliers.  In addition the user can request that  any
     of  a  set  of  reports  pertaining  to  the  input  data,  and  to
     intermediate calculations, be typed on his terminal.  The user  may
     also  obtain  graphs  on  a  suitable  graphics  terminal or with a
     plotter, if the graphics routines described below are  included  in
     the  program  and  used  as  directed.   These  operations  may  be
     performed in any order and as many times as desired in a particular
     session.

PENNZYME user's document                                          Page 2
BEGINNER'S GUIDE TO PENNZYME


     3.0  BEGINNER'S GUIDE TO PENNZYME

          The purpose of this section is to give the  user  who  has  no
     prior  experience  with  computers,  enough  information to use the
     program on an elementary level.

          PENNZYME is a program which fits the parameters in trial  rate
     laws   representing   possible  enzymatic  mechanisms  to  sets  of
     experimental initial velocity data.  It has considerable capability
     for  inputting  initial  guesses  ,  following  the  state  of  the
     computation, etc., which  the  sophisticated  user  can  employ  to
     efficiently  obtain  results interactively.  At the same time it is
     able to do without all of this and give the unsophisticated user  a
     result  with  minimal  assistance from him although the computation
     may then be  less  efficient.   Nonlinear  optimization  procedures
     generally  require  good  initial guesses for the parameter values.
     This program combines two  such  procedures  so  that  the  program
     effectively generates its own initial guesses if necessary(in which
     case many user inputs are set to default values).  A more  detailed
     description  is  given  in  the DETAILED DESCRIPTION section below.
     Technical terms are defined in the TECHNICAL GLOSSARY.

          To use the program two input  files  and  a  FORTRAN  function
     subroutine  representing  the trial rate law must be provided.  One
     of the two input files contains  the  experimental  velocity  data.
     The other file contains information which depends upon the rate law
     and the model to be tested and includes the initial values  of  the
     parameters  and  the selection indices and convergence criteria for
     the  fitting  algorithms.   The  experimental  velocity   data-file
     contains  only  the  chemical  names  and  concentrations  and  the
     observed enzymatic velocities.  Therefore, the  file  need  not  be
     changed  with  each  new  trial  model.  The user supplied rate law
     subroutine must be compiled and  linked  to  the  PENNZYME  package
     prior   to  operation  of  the  program.   A  description  of  this
     subroutine and the linking operation are given  below  under  "RATE
     LAW  SUBROUTINE".   The  parameter file and experimental data files
     described below must be  on  FORTRAN  logical  devices  1  and  20,
     respectively.   The  detailed  handling of the rate law file may be
     computer-dependent.

          The following discussion refers to the sample input files  for
     the  measurements and for the parameters which are shown in Fig 3.1
     and 3.2.  These files are actually read  by  the  program  in  this
     order,  and  may come from the same physical device, usually a disk
     file.  In this and the following discussion, input is described  as
     being  composed  of  files  made up of lines, which have presumably
     been typed in at a computer terminal.   (In  previous  versions  of
     this  program these were referred to as cards in a deck.) It should
     be noted that columns in the data input file may  be  separated  by
     tabs, but that this cannot be done in the parameter file, where ten
     spaces should be typed between columns.  An optional name  for  the
     velocity may be inserted in the data file on the line preceding the
     numerical values, but this will  not  carry  over  to  any  graphic
     output.

PENNZYME user's document                                          Page 3
BEGINNER'S GUIDE TO PENNZYME


     .c;Experimental Data Input File
     
            3,10
            SUBSTR 1
            SUBSTR 2
            INHIBITR
             1.2        5.0     3.5     1.11    .058
             1.2        5.0     35.0    .710    .034
             1.2        500.0   105.0   2.24    .115
             1.2        500.0   350.0   .766    .0426
             12.0       50.0    105.0   11.8    .6
             12.0       50.0    350.0   5.03    .258
             36.0       50.0    3.5     38.5    1.94
             36.0       50.0    35.0    36.0    1.64
             120.0      150.0   35.0    61.5    3.18
             120.0      150.0   105.0   57.9    2.76
                               FIGURE 3.1



     In this example the concentrations of three chemicals are  measured
     for  each  of  ten  velocity  observations.   The  next three lines
     contain the names of the three chemicals  of  our  example  in  the
     order in which they will be encountered in the velocity observation
     lines that follow.  This order  must  be  the  same  as  the  order
     assumed in the FORTRAN rate law which will be used.  The programmer
     supplying  the  rate  law  is   responsible   for   supplying   the
     documentation  needed  to determine this order.  In our example the
     chemical names are:

                         SUBSTR 1
                         SUBSTR 2
                         INHIBITR



     The next ten lines, in our example, each contains the data for  one
     velocity  observation.   Each of these lines contains the following
     information in the same order:

     1.  Concentrations of the measured chemicals in the same  order  as
         that in which their names were specified on the name lines.

     2.  Observed reaction velocity.

     3.  Experimental error of the velocity measurement.


     These numbers  may  appear  with  or  without  decimal  points  and
     exponents,  and  must be separated by either blanks or commas.  The
     following rule apply for input:

PENNZYME user's document                                          Page 4
BEGINNER'S GUIDE TO PENNZYME


     1.  All numbers are space delimited and may contain decimal  points
         and exponents.

     2.  Any names which are followed in the record by other input  must
         be padded with spaces to match the required character count.

     3.  Records must be placed in the input file in the required order,
         and are not numbered or otherwise identified.


          Optionally  the  position  normally  occupied  by  the   first
     experimental  point  may  be  occupied  by a set delimiter line, in
     which case the first  velocity  data  line  will  follow  the  last
     contiguous  delimiter line.  If the data cannot fit on one line, it
     may be placed on following contiguous records  provided  that  each
     line  but  the  last  has  exactly  "n"  values,  (where "n" is the
     "maximum values per record"  value  included  (optionally)  in  the
     first  record  of  the  file).  The last line must have at most "n"
     values but may have as few as one.

          Lines in the experimental file may be divided into sets.   Set
     delimiter   lines  may  beall  spaces  or  begin  with  non-numeric
     characters other than tab, decimal point, or space.   (These  lines
     may  also include comments for identification.) The program numbers
     the  data  sets  so  defined.   They  may   then   be   manipulated
     independtly.

          The numbers on the first of  these  lines  is  interpreted  as
     follows:

     line image:

        1.2      5      3.5     1.113     .0580


       Number               Interpretation       ______               ______________
        1.2             Concentration of "SUBSTR 1".
         5              Concentration of "SUBSTR 2".
        3.5             Concentration of "INHIBTOR".
       1.113            Observed reaction velocity.
       0.058            Experimental error of this measurement.
     The first line of the sample data file specifies the number of
     chemicals
     which have been measured in the experiment(and which appear in
     the rate law subroutine), and the number of steady state velocity
     measurements,
     in that order.

PENNZYME user's document                                          Page 5
BEGINNER'S GUIDE TO PENNZYME


     3.1  Rate Law Subroutine

          Prior to operation of the PENNZYME  program  a  user  supplied
     rate  law  subroutine must be compiled and linked with the PENNZYME
     package.   This  subroutine  must  be  a  FORTRAN  "REAL  FUNCTION"
     subroutine  and  must  be  named  "RATE".  Two argument vectors are
     passed  to  the  function  subroutine  and  contain   the   current
     concentration  values  and  the  current  parameter  values.  It is
     recommended that the argument vector names be the same for all user
     written  rate  law  subroutines.   A  sample rate law subroutine is
     provided in figure 5.1 .



             REAL FUNCTION RATE(PCONC,PARAM)
     
     
     
     
     C DUMMY VARIABLES:
     C   PCONC       CONCENTRATION ARRAY.
     C   PARAM       PARAMETER ARRAY.
     
             DIMENSION PCONC(1),PARAM(1)
             DATA QSMALL/1E-35/
     
     
             IF(PCONC(1).LE.QSMALL.OR.PCONC(2).LE.QSMALL.OR.PARAM(3)
             1               .LE.QSMALL) GO TO 100
     C----   ELSE, CALCULATE THE REACTION RATE.
                     QSUB1 = (PARAM(1)/PCONC(1))
                     QSUB2 = (PARAM(2)/PCONC(2))
                     QACTV = (PARAM(4)/PCONC(1))
                     QINHIB = (PCONC(3)/PARAM(3)) + 1.0
     
                     RATE = PARAM(5) / (QSUB1*QINHIB
             1                       + QSUB2*(QACTV*QINHIB+1) + 1)
                     GO TO 110
     C----   THEN, THE RATE WOULD HAVE BEEN ZERO.
       100           RATE = 0.0
       110   CONTINUE
     
     
     
             RETURN
     
             END



                               FIGURE 5.1

PENNZYME user's document                                          Page 6
BEGINNER'S GUIDE TO PENNZYME


     Notice  that   the   adjustable   parameters   and   the   chemical
     concentrations  are  represented  by  the  elements  of the vectors
     "PARAM" and "PCONC" respectively.  The order in which  they  appear
     in  these  vectors  must  correspond to the order in which they are
     specified in the input file.  Comparing the data file of figure 3.1
     with  the  rate  law subroutine of figure 3.2 we note the following
     correspondences:

      Vector element                 User label      ______ _______                 ____ _____

         PCONC(1)                      SUBSTR 1
         PCONC(2)                      SUBSTR 2
         PCONC(3)                      INHIBITR

         PARAM(1)                      KM1
         PARAM(2)                      KM2
         PARAM(3)                      KI
         PARAM(4)                      KA
         PARAM(5)                      VMAX
     The first line of the routine declares the program to be
     a "REAL FUNCTION" subroutine named "RATE", as required, with two
     arguments to be
     identified by the names "PCONC" and "PARAM".
     The next non-comment statement(i.e. statement without a "C" in
     column 1) is
     the "REAL" statement which declares that the two arguments are of
     variable type
     "REAL"(i.e. single precision floating point). The next statement
     declares that the 
     two argument names each refers to a vector of values. The first
     argument of the
     subroutine always refers to the vector of concentration values at
     which the rate
     of the reaction is to be calculated. The second argument refers to
     the vector of
     parameter values which, together with the rate law subroutine,
     complete our model
     of the enzymatic mechanism. It is these values that the
     optimization algorithms must
     determine.
     The rate law itself is written in algebraic equation form with the
     name of the
     function subroutine("RATE") on the left-hand side of the equation.
     PCONC(K), in our example, would refer to the concentration of the
     K'th chemical. PARAM(K) would refer to the value of the K'th rate
     law
     parameter value. The order of the chemicals and parameters may be
     defined
     arbitrarily when the rate  law subroutine is written, but if n
     chemicals
     are required they must be referenced as the 1 through n'th elements
     of the
     concentration vector. The same applies to the use of the parameter
     values vector.

PENNZYME user's document                                          Page 7
BEGINNER'S GUIDE TO PENNZYME


     The user should note that the concentration and parameter names and
     values supplied in the
     input data files must appear there in the same order in which they
     are
     referenced in the argument vectors of the rate law subroutine
     (i.e. the index numbers of the array elements correspond to the
     order of the input data).  It should be remembered that this
     routine will be called very many times in the course of the
     optimization calculation and should be as efficient as possible.
      In our example, additional statements are where included to
     check for small values of concentrations and parameters which would
     cause
     an "underflow" in the calculation of the reaction rate. This check
     is optional.

     For easier use of PENNZYME the user should have access to a library
     of  these  rate law subroutines, each with documentation explaining
     the  mechanism  it  represents  and  the   order   in   which   the
     concentrations  and  parameters  appear in their respective arrays.
     Cleland has published a large collection of rate laws together with
     definitions  of  their  Kinetic constants(Biochim.  Biophys.  Acta.
     67(1963) 104-137).  A  library  of  FORTRAN  implementations  of  a
     number  of  these  rate  laws,  in  the  format described above, is
     supplied with PENNZYME.  At the present time there are 28 rate laws
     in  this  library.   A  valuable tool for deriving rate laws is the
     KINAL program of Cornish-Bowden, Biochem.  J.  165(1977),55-59.

PENNZYME user's document                                          Page 8
BEGINNER'S GUIDE TO PENNZYME


          The Parameter File
                      Initial Estimates Input File
      15    THIS IS THE TITLE line.
      16    5
      17    KM1
      18    KM2         30.0
      19    KI
      20    KA
      21    VMAX        90.0
     
     
     c;FIGURE 3.2


     The parameter file starts with a  line  indicating  the  number  of
     adjustable parameters in the rate law model whose optimal values we
     wish to  determine.   In  our  example  there  are  five  of  these
     parameters.   The  next  five  lines-  one for each parameter- each
     contains the name and estimated value of a parameter.  The order of
     these  lines must be the same as the order required by the rate law
     subroutine being used.  The parameter name must  be  in  the  first
     eight  columns  of  the line.  The estimated value may start in any
     column from the ninth on.  The value is  represented  by  a  number
     with  or  without  a decimal point and exponent.  If no estimate is
     supplied by the user all columns past the eighth must be blank.  In
     our example the parameter names and values are:

        Name            Value        ____            _____
       "KM1"              0
       "KM2"             30
       "KI"               0
       "KA"               0
       "VMAX"            90

     A sample rate law subroutine for this data appears  in  figure  5.1
     (see also "RATE LAW SUBROUTINE" below).

PENNZYME user's document                                          Page 9
BEGINNER'S GUIDE TO PENNZYME


     
                               FIGURE 3.2






     3.1.1  Detailed Description Of Paramter Input File - 


     1.  Title Record: String of up to 60 characters which  will  appear
         in  output  report  headers.   Must  be the first record in the
         input file and should be centered within the first 60 character
         positions of the record.

     2.  Parameter Count Record: Number of adjustable parameters in  the
         rate  law.  Must be the second record of the file and may begin
         in any character position of the record.

     3.  Parameter Data Records: Contain the names and initial values of
         the  adjustable parameters of the rate law.  The first of these
         words must occupy the third record  position.   The  rest  must
         follow  in  contiguous  record  positions in the order in which
         they appear in the parameter array referenced in the  rate  law
         function  subprogram.   One must be present for each adjustable
         parameter as declared in record 2.  Format of the record is  as
         follows:

         1.  Parameter Name: Occupies record positions 1 through 8.

         2.  Parameter Value: Occupies any record positions past 8.


PENNZYME user's document                                         Page 10
program operation


         3.2  Program Operation

         3.2.1  MENU After processing the input data the program outputs
         a  message  indicating  the  current menu level and a prompt to
         enter the desired option.   Entering  the  option  "MENU"  will
         output the following:
         GRAPH    ENTER GRAPHICS MODE
         DEFN     ENTER PROBLEM DEFINITION MODE
             CONV      ALTER CONVERGENCE CRITERIA
                 SMPITER  SET MAX SIMPLEX ITERATIONS
                 DEVPAR   SET MAX RELATIVE DEV OF PARAMS FOR SIMPLEX
                 DEVERR   SET MAX REL. DEV OF LEAST-SQUARE-ERROR FOR SIMPLEX
                 STEP     SET INITIAL SIMPLEX STEP SIZE
                 FPITER   SET MAX FP ITERATIONS
                 ERREST   SET ESTIMATE OF EXPECTED LEAST SQUARE ERROR FOR FP
                 RELERR   SET MAX RELATIVE ERROR BETWEEN ITERATIONS FOR FP
             PARAM      ALTER PARAMETER VALUES
             DELOUT     DELETE OUTLIERS
             TRACE      SET FORMAT FOR TYPING TRACE OF OPTIM
                 SMPMODE  SET OUTPUT DEVICE FOR SIMPLEX REPORT
                 SMPPER   SET PERIOD BETWEEN TRACE OUTPUTS FOR SIMPLEX
                 FPMODE   SET OUTPUT DEVICE FOR FP REPORT
                 FPPER    SET PERIOD BETWEEN TRACE OUTPUTS FOR FP
                 RPTMODE  SET OUTPUT DEVICE FOR FINAL REPORTS
             FREEZE     FREE OR PIN PARAMETER VALUES
         OPTIM     ENTER PROBLEM OPTIMIZATION MODE
             SIMPLEX     PERFORM A SIMPLEX OPTIMIZATION
             FP          PERFORM A FLETCHER-POWELL OPTIM.
             SMPRPT      REPORT RESULTS OF SIMPLEX OPTIM
             FPRPT       REPORT RESULTS OF FLETCHER-POWELL OPTIM
             OUTLIER     DETERMINE AND OUTPUT OUTLIER DATA POINTS
         REPORT    ENTER REPORTS MENU
             DATA        LIST INPUT DATA
             RESID       OUTPUT RESIDUALS REPORT
             STATS       DETERMINE AND OUTPUT STATISTICAL REPORT
             PLIST       LIST PARAMETER VALUES
             VARCOV      OUTPUT VARIANCE-COVARIANCE MATRIX
         The  first word of every line is entered by the user to specify
         the desired action.  Entering an undefined option will generate
         an error message followed by Menu Desired?  (If so type "yes".)
         Responding with a yes will give a partial list of  the  options
         related to the current level.  This is followed by the message:
         Do you want menu of other levels?  A yes answer will  obtain  a
         list  of  the  options  that  are at the same level as the last
         option entered.  A valid option may be entered in  response  to
         either of the two questions and will then be executed.  

              Examples  of  individual  options  follow,  in  order   of
         increasing sophistication.

PENNZYME user's document                                         Page 11
program operation


         3.3  Program Output

         3.3.1  REPORT Submenu - 



         3.3.1.1  DATA Option (list Input Data) - 

              A sample report follows:

PENNZYME user's document                                                   Page 12
program operation


         **********************************************************************
         *             TEST OF PENNZYME: PENNSYLVANIA ENZYME PROGRAM          *
         *                             INPUT DATA                             *
         **********************************************************************
         
         
          NUMBER OF PARAMETERS     NUMBER OF CHEMICALS     NUMBER OF EXPERIMENTS
                      5                        3                      32
         
                                                             OBSERVED   STANDARD
                        CHEMICAL CONCENTRATIONS              VELOCITY   DEVIATION
         POINT       1         2         3        
         SET # 1
            1       1.2000    5.0000    3.5000                  1.0800     0.0930
            2       1.2000    5.0000   35.0000                  0.7300     0.0540
            3       1.2000    5.0000  110.0000                  0.3320     0.0270
            4       1.2000    5.0000  350.0000                  0.1330     0.0100
            5       1.2000   50.0000    3.5000                  5.8100     0.4100
            6       1.2000   50.0000   35.0000                  2.4400     0.2400
            7       1.2000   50.0000  110.0000                  1.5900     0.1200
            8       1.2000   50.0000  350.0000                  0.6300     0.0450
            9       1.2000  150.0000    3.5000                  7.7900     0.5500
           10       1.2000  150.0000   35.0000                  3.7800     0.3200
           11       1.2000  150.0000  110.0000                  1.9100     0.1600
           12       1.2000  150.0000  350.0000                  0.8190     0.0600
           13       1.2000  500.0000    3.5000                  7.4000     0.6300
           14       1.2000  500.0000   35.0000                  4.3200     0.3600
           15       1.2000  500.0000  110.0000                  2.1300     0.1800
           16       1.2000  500.0000  350.0000                  0.7150     0.0680
         SET # 2
           17      12.0000    5.0000    3.5000                  5.5500     0.4300
           18      12.0000    5.0000   35.0000                  4.1200     0.3200
           19      12.0000    5.0000  110.0000                  2.7400     0.2000
           20      12.0000    5.0000  350.0000                  1.2600     0.0930
           21      12.0000   50.0000    3.5000                 23.9000     2.1000
           22      12.0000   50.0000   35.0000                 18.5000     1.5000
           23      12.0000   50.0000  110.0000                 11.3000     0.9300
           24      12.0000   50.0000  350.0000                  4.9600     0.4100
           25      12.0000  150.0000    3.5000                 38.8000     3.0000
           26      12.0000  150.0000   35.0000                 26.3000     2.1000
           27      12.0000  150.0000  110.0000                 15.8000     1.3000
           28      12.0000  150.0000  350.0000                  6.6500     0.5500
           29      12.0000  500.0000    3.5000                 44.5000     3.5000
           30      12.0000  500.0000   35.0000                 28.9000     2.5000
           31      12.0000  500.0000  110.0000                 19.3000     1.5000
           32      12.0000  500.0000  350.0000                  7.9300     0.6300




PENNZYME user's document                                                   Page 13
program operation


         
         **********************************************************************
         *             TEST OF PENNZYME: PENNSYLVANIA ENZYME PROGRAM          *
         *                         STARTING VALUES                            *
         **********************************************************************
         
                             CURRENT LEAST-SQUARES ERROR:     6.12428E-01
         
         
                           INITIAL PARAMETER VALUES WERE:
                                KM1     1.00000E+01
                                KM2     1.00000E+01
                                KI      1.00000E+01
                                KA      1.00000E+01
                                VMAX    1.00000E+01




PENNZYME user's document                                                   Page 14
program operation


         3.3.2  OPTIM Submenu - 




         3.3.2.1  SIMPLEX Option (perform A Simplex Optimization) - 

              The Simplex method is  a  "robust"  method  and  does  not
         require  a  good  initial  estimate  to  locate a minimum.  Its
         convergence properties are less sensitive than gradient  search
         methods  to  curvature  of the least-squares error surface.  In
         addition, if there are several local minima the Simplex  method
         is  more  likely to find the global minimum rather than a local
         one, provided that the initial step size is chosen sufficiently
         large.



              3.3.2.2  SMPRPT Option (report Results Of Simplex Optimization) - 

              This report will be produced only  if  the  algorithm  has
         been  used  at  least  once  in  the  session.  A sample report
         follows:

PENNZYME user's document                                                   Page 15
program operation


         .rm 82
         
         ----------------------------------------------------------------------
         
         
                             FITTING BY SIMPLEX METHOD.
         
                        CONVERGENCE ACHIEVED AFTER 218 ITERATIONS.
                             -ELAPSED CPU TIME:    0 MIN  5.1 SEC
         
         
         RMS RELATIVE DEVIATION           TARGET            ACTUAL
         ABOUT THE CENTROID OF -
             -KINETIC PARAMETERS:       2.50000E-02       1.78445E-02
         
             -LEAST-SQUARES ERROR:      1.00000E-03       9.09281E-04
         
         
            LEAST-SQUARES ERROR:  START     6.12428E-01     END     4.85735E-02
            PERCENT REDUCTION:                  92.07%
         
         
                           OPTIMAL PARAMETER VALUES WERE:
                                KM1     1.17673E+01
                                KM2     4.75639E+01
                                KI      3.46474E+01
                                KA      6.76959E+00
                                VMAX    9.65884E+01
         



         This operation causes a least-squares fit of the velocity  data
         to  be  performed  by  the  Simplex  method  using  the current
         estimate of  the  optimal  parameter  values  and  the  current
         Simplex  option  values.  If the option values indicated that a
         trace report was



         3.3.2.3  FP Option (perform A Fletcher-Powell Optimization) - 

              The Fletcher-Powell method requires a good  initial  guess
         of  the  parameter  values  but  converges rapidly when such an
         estimate is supplied.  This initial estimate  is  automatically
         supplied  to  the  Fletcher-Powell  algorithm  when the Simplex
         method is used first.  Since it is a gradient search method  it
         can  detect the case where the Simplex method has converged but
         the least-squares error surface still has a calculable gradient
         allowing  the  fit  to be improved.  Trying to do optimizations
         with the Fletcher-Powell method alone can be quite expensive in
         computer usage.

PENNZYME user's document                                                   Page 16
program operation


              The recommended procedure  is  the  last  one;  locate  an
         initial  estimate by the Simplex method, then verify and refine
         this estimate by the Fletcher-Powell method.



              3.3.2.4  FPRPT Option (report Results Of Fletcher-Powell Optimization) - 

              This report will be produced only  if  the  algorithm  has
         been  used  at  least once during the session.  A sample report
         follows:



         .rm 82
         
         ----------------------------------------------------------------------
         
         
                             FITTING BY FLETCHER-POWELL METHOD.
         
                        CONVERGENCE ACHIEVED AFTER   8 ITERATIONS.
                             -ELAPSED CPU TIME:    0 MIN  3.8 SEC
         
         
         
            LEAST-SQUARES ERROR:  START     4.85735E-02     END     4.84583E-02
            PERCENT REDUCTION:                   0.24%
         
         
                           OPTIMAL PARAMETER VALUES WERE:
                                KM1     1.17010E+01
                                KM2     4.90328E+01
                                KI      3.46888E+01
                                KA      6.51458E+00
                                VMAX    9.61637E+01
         



                Fine Points in Using Fletcher-Powell Optimization


                        Starting Too Close to the Minimum
         A  warning  message  may  be  output  by  the   Fletcher-Powell
         optimization   routine:   CONVERGENCE   ACHIEVED   IN  TOO  FEW
         ITERATIONS TO ACHIEVE AN ACCURATE COVARIANCE MATRIX

         This means that the Fletcher-Powell optimization started at  or
         near  the  minimun  and  converged in fewer iterations than the
         number of parameters.  In this  situation  the  H  matrix  will
         either be calculated inaccurately or may never be calculated at
         all.  A tactic to get around this difficulty is  to  change  at
         least  two  and  preferably  all the paramter values by 10% and

PENNZYME user's document                                                   Page 17
program operation


         repeat the Fletcher-Powell optimization.  This tactic may  also
         be  useful  if  the  Fletcher-Powell optimization appears to be
         having difficulty finding the minimum--which may happen because
         it started out there.
                              Optimizing Error Model
         Input  to  the  PENNZYME  program  includes  estimates  of  the
         standard deviation of the velocity measurements.  These are not
         merely values obtained from a few replicate  measurements,  but
         are the standard deviations expected from hundreds of replicate
         measurements.  PENNZYME weights each squared  residual  by  the
         normalized   inverse   variance.    Clearly,  such  values  are
         available  only  if  a  particular  enzymatic  assay,  using  a
         particular instrumentation, had been previously calibrated.  If
         the standard deviations are set to zero, owing  to  a  lack  of
         information,  all  the  weights  are  set to unity and PENNZYME
         cannot use weighting  to  account  for  the  variation  in  the
         reliability  of  the  experimental  measurements.  The extended
         least squares option permits the user to estimate  the  unknown
         variance  simultaneously with identifying the optimal values of
         the kinetic parameters.

              Just as  the  user  must  supply  a  function  RATE  which
         calculates  the  expected  enzymatic velocity at a given set of
         ligand concentrations, to use extended least  squares  he  must
         also  supply  a  function  VARIAN which calculates the expected
         variance  of  a  given   experimental   velocity   measurement.
         PENNZYME  calls  VARIAN once for each data point.  The function
         arguments are:

              FUNCTION VARIAN (CONC,PARAM,VCALC) where

              CONC = array  of  ligand  concentrations  forcurrent  data
         point

              PARAM = array of error model parameters to be optimized

              VCALC = expected(i.e.  calculated) enzymatic velocity  for
         current

              data point.

              VARIAN  may  be  any  function  of  concentrations  and/or
         calculated  velocity, but usually it is a polynomial or a power
         law function of the expected velocity.  The  user  should  make
         some  attempt  at  obtaining  a  qualitative description of the
         error structure of his data.

              The  error  model  described  by   VARIAN   will   include
         adjustable  parameters  just as RATE does.  The parameter input
         file (on logical unit 1) must have initial estimates  of  these
         parameters  as well as the kinetic parameters.  For example, if
         the error model is a power law in the expected velocity: VARIAN
         = PARAM(1) * VCALC **PARAM(2)

PENNZYME user's document                                                   Page 18
program operation


              then initial estimates of error model parameters  PARAM(1)
         and  PARAM(2)  in  addition to those for the kinetic parameters
         are necessary.  The format for the parameter input file is:

              title

                kinetic parameters,  error parameters

              kinetic parameter name         <value>

              .                       .

              .                       .

              .                       .

              error model parameter name     <value>

              .                       .

              .                       .

              For the above example the input would resemble:

              title

              3,2

              KM     <VALUE>

              VMAX   <VALUE>

              KI     <VALUE>

              CONST  <VALUE>

              EXPON  <VALUE>

              VARIAN is called only if the extended least squares option
         is  set by including a nonzero number of error model parameters
         on the parameters input file.

              PENNZYME has a default error model: VARIAN  =  CONST**2  +
         VCALC**EXPON  where  CONST and EXPON are adjustable parameters.
         A user-supplied function overrides this default model.

              TO ENTER THE GRAPH MODE, TYPE GRAPH.   A  DETAILED  MANUAL
         FOR THE GRAPHICS COMMAND LANGUAGE FOLLOWS THE GLOSSARY BELOW.


                            The REPORTS level submenu



PENNZYME user's document                                                   Page 19
STATISTICS


         4.0  STATISTICS

              4.0.0.1  STATS Option (determine And Output Statistical Report) - 


              The  Statistics  Report  contains   statistical   measures
         relevent  to  the fitting calculation.  The form of this report
         depends upon which fitting algorithms were used, in what  order
         they  were used, and whether or not the calculations converged.
         A discussion of the statistical measures which appear  in  this
         report is given under "STATISTICS" below.

              PENNZYME computes the values of several  statistics  which
         serve  as  measures of the reliability of the optimal parameter
         values and as indicators of the presence of  systematic  errors
         (bias) in the kinetic model.


         Model Reliability         _____ ___________

     Residual error

                                   A measure of the model's fit  to  the
                              kinetic data.

     Pure error

                                   The residual error expected  if  only
                              experimental     errors     of    velocity
                              measurements determine the residuals.

     Excess variance

                                   (Residual error)**2 - (Pure error)**2
                              .   A measure of bias.  The ratio of these
                              two  squared  terms  may  be  used  as  an
                              "F-test"   to   determine  if  the  excess
                              variance is significant.

     Parameter Reliability     _________ ___________

     Standard deviation

                                   A measure of  the  curvature  of  the
                              error  surface  in  the  vicinity  of  the
                              minimum.   Small  values   indicate   high
                              curvature and a well defined minimum.

     95% confidence limit

                                   The value which when subtracted  from
                              or  added  to  the optimal parameter value
                              defines the range of values in which there
                              is  a  95% probability of finding the true

PENNZYME user's document                                                   Page 20
STATISTICS


                              parameter value.

     T-statistic

                                   The ratio (parameter value / standard
                              deviation).   If this ratio is less than a
                              certain value, the corresponding parameter
                              value  is not significantly different from
                              zero,  and  the  parameter  is  redundant.
                              PENNZYME performs this test automatically.



     **********************************************************************
     *             TEST OF PENNZYME: PENNSYLVANIA ENZYME PROGRAM          *
     *                         STATISTICS REPORT                          *
     **********************************************************************
     
     
     
     
     PURE ERROR:        2.78787E-01
     RESIDUAL ERROR:    4.84583E-02
     AVERAGE OBSERVED VELOCITY:                            9.44122E+00
     (RES. ERR.)/(AV. VEL.) = RELATIVE ERROR:              5.13264E-03
     (RES. ERR.)**2 - (PURE ERR.)**2 = EXCESS VARIANCE:   -7.53738E-02
     (RES. ERR.)**2 / (PURE ERR.)**2 = MEASURE OF BIAS:    3.02130E-02
     
     
     PARAMETER
        NAME        VALUE     STD. DEV.  CNFD. LIM.  T-STATISTIC     < T(.95)
     
      KM1        1.17010E+01  1.866E+00  3.830E+00   6.26950E+00         
      KM2        4.90328E+01  9.786E+00  2.008E+01   5.01032E+00         
      KI         3.46888E+01  2.196E+00  4.506E+00   1.57980E+01         
      KA         6.51458E+00  1.057E+00  2.169E+00   6.16224E+00         
      VMAX       9.61637E+01  1.202E+01  2.466E+01   8.00187E+00         



     An arrow("<---") will appear in the  column  directly  beneath  the
     header " , t(.95)" for any parameters whose t-Statistic exceeds the
     95% confidence limit.  If the arrow appears for a parameter  it  is
     likely that the parameter is redundant for the data set used.



     4.0.0.2  RESID Option (output Residuals Report) - 

          A sample report follows:

PENNZYME user's document                                                   Page 21
STATISTICS


     **********************************************************************
     
     *     RAPID-EQUILIBRIUM BINARY REACTION WITH HILL COEFFICIENTS       *
     *                             RESIDUALS REPORT.                      *
     
     **********************************************************************
     
     
        OBS     V(CALC)V(OBS)     V(CALC)    WEIGHT   WEIGHTED
                                      -V(OBS)             RESIDUAL
     SET # 1
         1    1.5O1E-O1  1.5O4E-O1  -2.946E-O4  1.73OE+OO  -5.O98E-O4
         2    1.869E-O1  1.9O5E-O1  -3.6O8E-O3  1.551E+OO  -5.597E-O3
         3    2.473E-O1  2.451E-O1   2.221E-O3  1.173E+OO   2.604E-O3
         4    3.658E-O1  3.69OE-O1  -3.236E-O3  6.120E-O1  -1.981E-O3
         5    5.7O8E-O1  6.25OE-O1  -5.423E-O2  2.469E-O1  -1.339E-O2
     SET # 2
         6    1.672E-O1  1.7O2E-O1  -3.OO8E-O3  1.656E+OO  -4.98OE-O3
         7    2.O82E-O1  2.O51E-O1   3.O66E-O3  1.422E+OO   4.361E-O3
         8    2.755E-O1  2.667E-O1   8.774E-O2  1.OO6E+OO   8.822E-O3
         9    4.O74E-O1  3.883E-O1   1.91OE-O2  4.954E-O1   9.462E-O3
        1O    6.357E-O1  6.25OE-O1   1.O75E-O2  1.965E-O1   2.112E-O3
     SET # 3
        11    1.87OE-O1  1.923E-O1  -5.282E-O3  1.55OE+OO  -8.19OE-O3
        12    2.328E-O1  2.235E-O1   9.35OE-O3  1.264E+OO   1.182E-O2
        13    3.O81E-O1  3.OO8E-O1   7.339E-O3  8.375E-O1   6.146E-O3
        14    4.557E-O1  4.2554E-O1  3.O21E-O2  3.948E-O1   1.193E-O2
        15    7.111E-O1  7.519E-O1  -4.O77E-O2  1.548E-O1  -6.313E-O3
     SET # 4
        16    2.O94E-O1  2.128E-O1  -3.384E-O3  1.414E+OO  -4.787E-O3
        17    2.6O7E-O1  2.516E-O1   9.137E-O3  1.O91E+OO   9.967E-O3
        18    3.45OE-O1  3.419E-O1   3.143E-O3  6.835E-O1   2.148E-O3
        19    5.1O3E-O1  4.819E-O1   2.839E-O2  3.123E-O1   8.866E-O3
        2O    7.963E-O1  8.696E-O1  -7.33OE-O2  1.216E-O1  -8.915E-O3
     SET # 5  
        21    2.263E-O1  2.439E.O1  -1.757E-O2  1.306E+OO  -2.294E-O2<--
        22    2.818E-O1  2.721E-O1   9.7O1E-O3  9.7O6E-O1   9.416E-O3
        23    3.729E-O1  3.883E-O1  -1.538E-O2  5.896E-O1  -9.O7OE-O3
        24    5.515E-O1  5.714E-O1  -1.989E-O2  2.654E-O1  -5.279E-O3
        25    8.6O6E-O1  1.O2OE+OO  -1.598E-O1  1.O3OE-O1  -1.646E-O2
     
                       CURRENT LEAST-SQUARES ERROR;      1.O625OE-O2
     
                  CURRENT PARAMETER VALUES WERE:
                      KMPEP     2.97865E+O1
                      KMADP     1.838O7E+O2
                      VMAX      1.O787OE+OO
                      HCPEP     1.2O112E+OO
                      SIG       3.96878E-O2
                      ALPHA     4.29188E+OO



     The markers "  <---  "  at  the  right  margin  flag  those  POINTS

PENNZYME user's document                                                   Page 22
STATISTICS


     identified  as  outliers  by  the program (see index 8 above).  The
     message "DELETED" appears in the same position for any points which
     were  removed  from  the fitting calculation by the user, using the
     DELOUT option which is described below.  (When the marker " <---  "
     appears   in  any  report  involving  parameters,  it  indicates  a
     parameter which is not  significantly  different  from  zero  in  a
     statistics  report,  and  a  parameter which is pinned in any other
     report involving parameters.)



     4.0.0.3  OUTLIER Option (determine And Output Outlier Data Points) - 

          This operation compares the absolute  value  of  the  weighted
     residuals   to   twice   the   standard  error.   Any  observations
     (data-points)  whose  weighed  residuals  exceed  this  limit   are
     numbered,  inserted  in  an internal "outlier table" and printed on
     the user's terminal.  There is room in the table for ten  outliers.
     If more than this are found a warning message and the number of the
     velocity observation is printed for each outlier for which there is
     no room in the table.  A sample report follows:



     ENTER DESIRED OPTION > OUTLIER
     
     OUTLIER  DATA POINT      V(OBS)         RESIDUAL
     
        1          6       2.63900E+00      3.37986E-01
        2         56       2.42100E+01      2.77115E+00
     ENTER DESIRED OPTION >






     4.0.0.4  PLIST Option (list Parameter Values) - 

          This operation produces the following report:



     ENTER DESIRED OPTION > PLIST
     
     
                       CURRENT PARAMETER VALUES WERE:
                            KM1       1.24335E+01
                            KM2       5.06060E+01
                            KI        3.54142E+01
                            KA        6.91388E+00
                            VMAX      1.01837E+02
     .s2
     (The marker " <--- " indicates a pinned parameter.)

PENNZYME user's document                                                   Page 23
STATISTICS


     .s2
     ENTER DESIRED OPTION > VARCOV
     .b3
     This option prints out the variance -covariance matrix.
     
     
     
     ****************************************************************
     * RAPID EQUILIBRIUM BINARY REACTION WITH HILL COEFFICIENTS     *  
     *                         VAR-COVAR MATRIX                     *
     ****************************************************************
        KMPEP       KMADP       VMAX        HCPEP
      1.2454E+01  1.2915E+00  1.8991E-01 -2.2180E-01  KMPEP
                  7.2989E+01  2.6871E-01 -4.0922E-03  KMADP
                              6.6961E-03 -1.0788E-02  VMAX
                                          2.3825E-02  HCPEP
     
     
     
     
     
     ****************************************************************
     * RAPID-EQUILIBRIUM BINARY REACTION WITH HILL COEFFICIENTS     *
     *                     NORM. VAR-COVAR MATRIX                   *
     ****************************************************************
        KMPEP       KMADP       VMAX        HCPEP
      1.0000E+00  4.2836E-02  6.5762E-01 -4.0720E-01  KMPEP
                  1.0000E+00  3.8436E-01 -3.1032E-03  KMADP
                              1.0000E+00 -8.5410E-01  VMAX
                                          1.0000E+00  HCPEP
     

PENNZYME user's document                                                   Page 24
STATISTICS


     4.0.1  DEFN (PROBLEM DEFINITION) Submenu - 



     4.0.1.1  CONV Option (alter Convergence Criteria) - 

          This  operation  allows  the  user  to  alter  the  values  of
     variables which were initialized from data in the "method specific"
     input file.  These variables are described in  the  section  "INPUT
     DATA".   The  following  is a sample of the dialogue which the user
     will encounter:

          Notice that the user may examine a  variable's  value  without
     changing  the  value by entering "n" in response to the "new value"
     prompt.  Also note that the variable types  are  mixed.   The  user
     need  not  know  the  type of a particular variable (although it is
     hoped that he would) since the type  conversion  of  user  supplied
     data is done automatically.



     4.0.1.1.1  Index 3 - "Delete An Outlier" - 


          "Outlier deletion" is an operation which allows  the  user  to
     remove from the fitting calculation points whose weighted residuals
     exceed twice the least-squares error.  This is done by removing the
     weights  of  these  points and renormalizing the remaining weights.
     Points which have been deleted may be returned to  the  calculation
     by the reverse operation "Reinsert a deleted point".  Both of these
     operations are provided in a control subsection initiated by  entry
     of  index  value  3  in  response  to the options prompt.  A sample
     dialogue follows:



     ENTER DESIRED OPTION >
     
     MANIPULATE OUTLIERS.
     PIN
     (describe here pinning parameters)
     .hl4PARAM option (alter parameter values)
     
     This operation is provided to allow the user to adjust his estimate
     of the optimal parameter values prior to or between fitting
     attempts. Sample dialogue follows:
     
     .tp40
     .b3;.lt
     ENTER DESIRED OPTION > PARAM
     
     ALTER PARAMETERS.
     PLEASE ENTER PARAMETR INDEX(OR <CR>):2
     

PENNZYME user's document                                                   Page 25
STATISTICS


     PARAMETR  KM2     IS   10.00000
     ENTER NEW VALUE (OR N, FOR NO CHANGE):50
     
     PLEASE ENTER PARAMETR INDEX(OR <CR>):4
     
     PARAMETR  KA      IS   10.00000
     ENTER NEW VALUE (OR N, FOR NO CHANGE):N
     
     PLEASE ENTER PARAMETR INDEX(OR <CR>):97
     
     INDEX 97 IS OUT OF BOUNDS, TYPE <CR> FOR A LIST OF OPTIONS.
     PLEASE ENTER PARAMETR INDEX(OR <CR>):5
     
     PARAMETR  VMAX    IS   10.00000
     ENTER NEW VALUE (OR N, FOR NO CHANGE):97
     
     PLEASE ENTER PARAMETR INDEX(OR <CR>):
     
     (ENTER "-1" IF NO MORE CHANGES)
     INDEX    PARAMETER NAME    VALUE
     
       1         KM1       1.00000E+01
       2         KM2       5.00000E+01
       3         KI        3.00000E+01
       4         KA        1.00000E+01
       5         VMAX      9.70000E+01
     
     PLEASE ENTER PARAMETR INDEX(OR <CR>):-1
     
     'BYE!
     PLEASE ENTER CONTROL  INDEX(OR <CR>):




          Notice the mistake made by the user in selecting the parameter
     index.   The  number  entered  ("97")  was meant to be the value of
     parameter #5 rather than a parameter index.



          4.0.1.2  TRACE Option (set Format For Typing Trace Of Optim) - I
     f  the option values indicated that a trace report was to appear on
     the user's terminal it will be typed at this point.  See the sample
     session  dialogue  for  a  typical  trace  report.   Upon return to
     interactive mode the parameter values will be the optimal values as
     determined  by  the  fitting  operation.   A  sample  trace  report
     follows:

PENNZYME user's document                                                   Page 26
STATISTICS


     **********************************************************************
     *             TEST OF PENNZYME: PENNSYLVANIA ENZYME PROGRAM          *
     *                     SIMPLEX TRACE REPORT.                          *
     **********************************************************************
     
     
     
     ITERATION 25    RMS RELATIVE DEVIATION OF KINETIC PARAMETERS 1.29966E-01
     
     
                         CURRENT LEAST-SQUARES ERROR:     1.32720E-01
     
     
                       CURRENT PARAMETER VALUES WERE:
                            KM1     2.53438E+00
                            KM2     7.25742E+00
                            KI      2.79929E+01
                            KA      1.79910E+01
                            VMAX    3.24603E+01
     
     
     
     ITERATION 50    RMS RELATIVE DEVIATION OF KINETIC PARAMETERS 3.44595E-02
     
     
                         CURRENT LEAST-SQUARES ERROR:     1.11128E-01
     
     
                       CURRENT PARAMETER VALUES WERE:
                            KM1     4.09943E+00
                            KM2     6.96557E+00
                            KI      3.77969E+01
                            KA      2.00883E+01
                            VMAX    3.63544E+01



     A least-squares fit is found by the Fletcher-Powell gradient search
     method,  using the current estimate of the optimal parameter values
     as a starting estimate, and using the current  values  of  the  F-P
     option selection indices.  A trace report is produced on the user's
     terminal if selected through the F-P option values.  A sample trace
     report follows:

PENNZYME user's document                                                   Page 27
STATISTICS


     **********************************************************************
     *             TEST OF PENNZYME: PENNSYLVANIA ENZYME PROGRAM          *
     *                 FLETCHER-POWELL TRACE REPORT.                      *
     **********************************************************************
     ITERATION  3
     
                         CURRENT LEAST-SQUARES ERROR:     4.45696E-02
     
     
                       CURRENT PARAMETER VALUES WERE:
                            KM1     1.17266E+01
                            KM2     4.77989E+01
                            KI      3.48247E+01
                            KA      6.77243E+00
                            VMAX    9.62696E+01
     ITERATION  6
     
                         CURRENT LEAST-SQUARES ERROR:     4.45120E-02
     
     
                       CURRENT PARAMETER VALUES WERE:
                            KM1     1.17035E+01
                            KM2     4.90169E+01
                            KI      3.46901E+01
                            KA      6.51486E+00
                            VMAX    9.61774E+01




PENNZYME user's document                                                   Page 28
STATISTICS


 4.  Program Mode Record: Contains  data  which  indicates  the  initial
     optimization  strategy and the report generation mode.  This record
     must follow the last parameter data record and  has  the  following
     internal format:

     1.  Simplex Selector: Must be first value in record.  If  value  is
         greater  than  or  equal  to zero then a Simplex mode record is
         expected.

     2.  Fletcher-Powell Selector: Must be second value in  record.   If
         value  is  greater than or equal to zero then a Fletcher-Powell
         mode record is expected, and the  Fletcher-Powell  mode  record
         must follow the:

         1.  Program Mode Record if the Simplex selector value  is  less
             than zero.

         2.  Simplex Mode  Record  if  the  Simplex  selector  value  is
             greater than or equal to zero.


     3.  Report Mode Indicator: Must be third number in record.  If  its
         value is "2" the residuals report will be included in the final
         report.


 5.  Simplex Mode Record: Contains input relevant to use of the  Simplex
     algorithm.   All  of  the  following numbers must be present in the
     indicated order.  A value of zero for any  number  will  cause  the
     indicated default values to be used.

     1.  Maximum iterations of algorithm allowed.  
         Default: 50 + 40 * number-of-adjustable-parameters

     2.  Initial Simplex Step Size.  Should be large  enough  to  assure
         that   the  minimum  will  be  reached  before  contraction  is
         completed.  It is  expressed  as  a  fraction  of  the  initial
         parameter values.
         Default: 1.0

     3.  Convergence Mode.
         = 1, Test for convergence will be on the RMS relative deviation
         of  the  parameters  of  the  Simplex  from  those defining the
         centroid.
         = 2, Test for convergence will be on the RMS relative deviation
         of  the  least-squares  errors  of  the vertices of the simplex
         about that of the centroid.
         = 3, Both of the above must be satisfied.
         Default: 1

     4.  Convergence criterion "a".  Convergence criterion for test #1 .
         Default: 0.05 

PENNZYME user's document                                                   Page 29
STATISTICS


     5.  Convergence criterion "b".  Convergence criterion for test #2 .
         Default: 0.05 

     6.  Trace mode.
         = -1, no trace report.
         = 0, same as 1 (default).
         = 1, trace report on user's console.
         = 2, trace report on printer.
         = 3, trace report in both locations.
         Default: 0 

     7.  Trace period.  Number of iterations  to  be  performed  between
         trace printouts.  
         Default: 25


 6.  Fletcher-Powell Mode Record: Contains input relevant to use of  the
     Fletcher-Powell algorithm.

     1.  Maximum iterations of algorithm allowed.  
         Default: 10 * number-of-adjustable-parameters

     2.  Estimate of minimum sum of squared errors obtainable.
         Default: 0

     3.  Expected relative error of the parameters.  
         Default: 1 * 10**(-6)

     4.  Trace mode.  Same options as for Simplex.  
         Default: 0

     5.  Trace period.  Number of iterations  to  be  performed  between
         trace printouts.
         Default: 5





          4.0.1.3  Simplex And Fletcher-Powell Mode Record Contents - 



                     Simplex Mode Record Contents:

               1.  Max.  iterations of algorithm allowed,

               2.  initial Simplex step size,

               3.  convergence mode,

               4.  convergence criterion "a",

PENNZYME user's document                                                   Page 30
STATISTICS


               5.  convergence criterion "b",

               6.  trace mode,

               7.  number of iterations between trace printouts.




                 Fletcher-Powell Mode Record Contents:

               1.  Max.  iterations of algorithm allowed,

               2.  estimate  of  the  minimum  sum  of  squared   errors
                   obtainable,

               3.  expected relative error of the parameters,

               4.  trace mode,

               5.  number of iterations between trace printouts.


PENNZYME user's document                                                   Page 31
STATISTICS


     4.0.1.4  Description Of Simplex And Fletcher-Powell "Mode Record" Variables: - 



     Variable                           Description     ________                           ___________

                     Simplex specific:                     _______ _________

Max.  iterations              A good rule of thumb for this algorithm is
                              50  iterations  plus 40 for each parameter
                              to be fit.

Initial step size             This should be large enough to enclose the
                              minimum  error  point in parameter space .
                              It is  expressed  as  a  fraction  of  the
                              initial parameter estimate.

Convergence mode              = 1, test for convergence will be on
                                  the RMS relative deviation of
                                  the parameters of the Simplex from
                                  those of the centroid.
                              = 2, test for convergence will be on
                                  the RMS relative deviation of the
                                  least-squares errors of vertices
                                  of the Simplex about that of the
                                  centroid.
                              = 3, both of the above must be satisfied.

Criterion "a"                 Maximum allowable  RMS  deviation  of  the
                              parameter  values  of the simplex vertices
                              and   centroid   for   convergence   under
                              convergence modes 1 and 3.

Criterion "b"                 Maximum   allowable   RMS   deviation   of
                              least-squares   errors   of   the  simplex
                              vertices  and  centroid  for   convergence
                              under convergence modes 2 and 3.

Trace mode                    = -1, no trace report.
                              =  0, same as 1 (default).
                              =  1, trace report on user's console.
                              =  2, trace report on printer.
                              =  3, trace report at both locations.

Trace period                  Number  of  iterations  to  be   performed
                              between trace printouts.

                 Fletcher-Powell specific:                 _______________ _________

Max.  iterations              A good rule of thumb is 10 iterations  for
                              each parameter.

Est.  of sum of squares       If this is not known use "0" .

PENNZYME user's document                                                   Page 32
STATISTICS


Est.  of error                Not less than 10**(-6).

Trace mode                    See Simplex specific.

Trace period                  See Simplex specific.




PENNZYME user's document                                                   Page 33
TECHNICAL GLOSSARY


                              5.0  TECHNICAL GLOSSARY





     Centroid                 The centroid of all the  vertices  of  the
                              simplex  but  the  one  with  the  largest
                              least-squares error.

     Convergence criteria     Conditions which must be fulfilled for  an
                              iterative  calculation to be considered to
                              have converged.

     Gradient search method   An  optimization  method  which  uses  the
                              gradient  of  a  function  to  locate  the
                              extrema of the function.

     Parameter                Rate law  constant  to  be  calculated  by
                              PENNZYME which will result in the best fit
                              of the experimental data by the  rate  law
                              type.

     Parameter space          The n-dimensional space defined by  the  n
                              different rate law parameter variables.

     Record                   A collection  of  related  items  of  data
                              treated as a unit.

     Residual                 Difference between calculated and observed
                              velocity values.

     Run-time                 The interval during which the  program  is
                              executing.

     Simplex                  The n+1 points in parameter space(where  n
                              is  the  number  of  parameters) which are
                              used by the Simplex  algorithm  to  locate
                              the error function minimum.

     Vector                   A variable type consisting of  an  ordered
                              set of values.

     Vertices                 The individual points defining a simplex.





     1.0  GRAPHICS COMMANDS

          There are three types of commands currently implemented in the
     graphics system.  They are the Setup, Graph-Type and Data-Selection
     commands.  All command types use the same general input  format  to
     minimize the number of special cases the user must remember.

          The Setup commands define the general physical  appearance  of
     the  graph.   They  are used to specify the size of the graph, axis
     numbering and labelling, etc.  The data is organized  as  a  table,
     each  line  containing  the  values of the variables to be graphed.
     For PENNZYME the data is organized as  lines  of  data,  the  first
     columns being the various chemical concentrations.  The next column
     contains the observed velocities at  the  chemical  concentrations;
     the  last  column  contains the standard deviations associated with
     the observed  velocities.   The  Graph-Type  commands  specify  the
     variables  (columns)  to  be  graphed.   Unless  restricted  by the
     Data-Selection commands, all the lines of data will  be  used  when
     graphing.

          The Graph-Type commands  thus  specify  the  variables  to  be
     graphed  and  also  the  type of representation that is to be used.
     These include displaying data as discrete or connected points, with
     or without error bars and displaying several related curves at once
     as in the case of PENNZYME specific graphics.

          The Data-Selection commands allow the user to define the range
     of  data  points to be graphed for each individual curve.  The data
     points can be selected by  input  line  using  expressions  of  the
     following  type:  all  points  up  to  line  24, points from line 2
     through line 32.  They can also be selected by  specifying  a  data
     set number.  This selects one or several of predefined data subsets
     such as those defined in PENNZYME.  One can also select data  lines
     by  having any line for which the value of a variabale matches that
     specified.  For example, include all lines for which Mgconc = 3.O.

          The complexity of the commands  varies  from  Setup  commands,
     usually  a  simple assign statement (set x-axis length to 8 inches)
     to the Graph-type commands where the  user  must  include  variable
     names  for the x, y and error components, separated by operators as
     well as any optional switches.  In between these two  extremes  lie
     the  Data-Selection  commands  where the user enters an expression,
     usually a series of line numbers separated by commas.

          In all of the commands, the first word  must  be  the  command
     specifier.   There  are  currently  l5  of  these  including  those
     implemented  for  PENNZYME.   All  of  the   commands,   variables,
     operators  and  switches  can be entered by the user as unambiguous
     abbreviations of their full representation.  They are all separated
     by  blank  characters  except  for  the  variable names which allow
     imbedded blanks and therefore are  terminated  by  an  operator,  a
     switch,  etc.   Command  specifiers  and switches can optionally be
     terminated by an equals sign.  This makes for a more  sentence-like
     command  line when using the Setup commands and some switches where

PENNZYME user's document                                          Page 2
GRAPHICS COMMANDS


     a value is being assigned ('XLENGTH  =  8').   Variable  names  are
     those  defined  by  the user either as specified to the stand-alone
     graphics or as specified by a host program.  Additional  names  can
     be defined for quantities previously unnamed in the host system but
     graphed in the graphics system.  This is  described  later  in  the
     description   of  the  interfacing  routine.   As  an  example,  in
     PENNZYME, quantities were not assigned names by the user since only
     chemical   names   are  required.   These  were  the  observed  and
     calculated velocities, the associated standard deviations  and  the
     residuals.   They  were then assigned the names 'VELOCITY', 'VCALC'
     'ERROR' and 'RESIDUAL' in the interfacing routines.

          Operators are used to separate variable names and to  indicate
     the  relationship  between  variables.   For  example,  the  '.VS.'
     operator indicates that the first variable is to  be  the  ordinate
     and  the  second  one  the abscissa.  The '.ERR.' operator uses the
     next variable to generate error bars.  Operators must  be  enclosed
     by  periods  to  indicate  that  they  are not part of the variable
     names.

          A switch is text entered by the user at the end of  a  command
     which  modifies the value of a graph parameter.  The parameters are
     initially set to default values and reset to these values when  the
     switch  is  turned  off.   The effect of a switch is limited to the
     command to which it is appended.  If it  is  appended  to  a  setup
     command,  it will stay active until turned off.  When appended to a
     graph-type command, it is only active for that command and does not
     affect  succeeding similar graph-type commands.  The general format
     of a switch is a slash (/) followed by the switch name, which is of
     the  same  format  as the command specifiers.  If required, this is
     followed by a value to be assigned to  the  switch.   One  or  more
     switches may be used in a command, each being separated by a slash.
     Switches are meant to be used to alter a convenient default  value.
     If  the  default values are often inappropriate then they should be
     modified within the program.   Defaults  for  setup  commands,  for
     example,  are  set  once for the entire program whereas the default
     symbols for the graph-type commands are rotated through  the  eight
     special symbols.



     1.1  Overview Of Process Of Generating A Graph

          The graphics  were  designed  for  use  with  a  storage  tube
     graphics  display.   This  requires  that  the  user  enter all the
     commands and that they be processed before the graph is  initiated:
     otherwise,  this  would require partial erasure of the screen which
     is not possible on storage tubes.

          In a typical graph, the user would not change the defaults for
     the  axis  lengths  and  origins.  It might be desired, however, to
     label the axes, and this would be done  using  the  label  commands
     followed by a literal string containing the text of the label.  All
     of the setup commands can be entered at anytime prior to the actual

PENNZYME user's document                                          Page 3
GRAPHICS COMMANDS


     graphing  since  they only take effect after all the other commands
     have been entered.  At this point the command  to  define  a  curve
     would  be  entered.   In the simplest of cases this consists of the
     DRAW command:


          DRAW Y .VS.  X 


          Entering the'PLOT' command will then display a graph using the
     entire  range  of  points  and  connecting  them with straight line
     segments.   The  scaling  and  numbering  of  the  axes  would   be
     calculated  to  insure the largest graph possible while maintaining
     reasonable axis numbering  values.   The  appropriate  axis  labels
     would also be displayed.

          The data selection command was designed to allow the  user  to
     define   the  range  of  data  to  be  graphed  and  also  to  make
     specification  of  multiple  curve  graphs  quicker.   The  typical
     'SELECT' command would be of the type:


          SELECT  1-15,16-18


          Select rows 1 through 15 and 16 through 18 for  display.   The
     select  command  must be entered after the graph-type command it is
     to modify.  If several curves of the  same  variables  were  to  be
     graphed  then  one  could  alternate between the graph-type and the
     select commands for each curve.  For a  family  of  4  curves  this
     would  require  8  command  lines.   To reduce this, the graph-type
     command can be entered  only  once  and  each  subsequent  'SELECT'
     command  will  refer  to that graph-type command.  This reduces the
     number of commands to 5 lines, one for the graph-type followed by 4
     'SELECT'  commands.   When  this  feature  is  used  for displaying
     families of points, the symbol defaults are  automatically  rotated
     through the eight available special symbols for each set of points.



     1.2  Description Of Graphic Commands And Their Effects

          These consist of three basic types: LABEL, ORIGIN, and LENGTH.
     Each  of  these  must be prefixed by an 'X' or a 'Y' to specify the
     axis being set (e.g., 'XLABEL').  These are input  in  response  to
     the prompt [] from the program.


          LABEL command


          The 'LABEL' command  draws  up  to  50  characters  (including
     blanks)  of  text  centered below or alongside the designated axis.
     If no label command is entered, no label will be drawn.  Once it is

PENNZYME user's document                                          Page 4
GRAPHICS COMMANDS


     defined,  it will appear on every succeeding graph until removed by
     a new label command.

     [] XLABEL = 'X-AXIS'
     [] YLAB = carriage return (Remove YLABEL)


          ORIGIN command


          The 'ORIGIN' command permits the user to place the lower  left
     corner  of  the graph at any distance in inches from the lower left
     corner of the physical screen.  This is useful for moving the graph
     around  to  ensure  best placement of the graph within the physical
     limits of the  screen.   This  is  required  when  using  different
     terminals  which  have  different  characteristics.   The  'ORIGIN'
     command does not affect the values at the origin of  the  variables
     graphed.

     [] XORIGIN = O.5
     [] YOR  =  carriage return (Reset to default  value)


          LENGTH command


          The 'LENGTH' command specifies  the  length  of  the  axis  in
     inches  from  the  point  defined  by  default  or  by the 'ORIGIN'
     COMMAND.  The switch 'NUMBER' may be used to ensure or inhibit ('NO
     NUMBER') the output of axis numbering.

     [] XLENGTH = 7
     []YLEN = 6/NO NUMB


          GRAPH-TYPE commands


          These consist of the two basic commands;  'DRAW'  and  'POINT'
     plus  those  defined specifically for use with PENNZYME; 'FITPLOT',
     'RESIDPLT' and 'CALC'.


          DRAW and POINT commands


          The 'DRAW' command will generate a graph of y  vs.   x,  using
     the  data  values  of  the  first  variabale for y and those of the
     second variable for x.  The two  variables  are  separated  by  the
     '.VS.'  operator.  The 'DRAW' command connects each point by a line
     segment without representing the  data  point  by  a  symbol.   The
     'POINT' command displays the data as unconnected symbols.  If error
     bars are desired, then a third variable must be  specified  by  the
     'ERR' operator.

PENNZYME user's document                                          Page 5
GRAPHICS COMMANDS


     [] DRAW YVAR .VS. XVAR
     [] DRAW YVAR .VS. XVAR .ERR. STDEV
     [] POINT YVAR. VS. XVAR


          FITPLOT command


          The 'FITPLOT' command is the most often used by  the  PENNZYME
     user.   It  generates  a  graph  like that specified by the 'POINT'
     command and then superimposes  a  curve  of  calculated  velocities
     interpolated  polated  over the range of the chemical concentration
     variable specified.  The velocities are calculated using  the  rate
     law  function  linked  to PENNZYME.  This graph only makes sense if
     the velocity is the  ordinate  and  a  chemical  concentration  the
     abscissa.   All  other chemical concentrations should be fixed over
     the range that is being graphed.  No checking is performed  by  the
     program  for  nonsensical graphs.  A warning message is issued when
     more than one chemical concentration is varied.  The user then  has
     the option of completing the graph or starting over.

     [] FITPLOT VEL .VS. CHEMCON
     [] FITPLOT VEL .VS. CHEMCON .ERR. STDEV


          RESIDPLT Command


          The 'RESIDPLT' command is used to display the systematic error
     of  a model and the systematic and random error of the experimental
     data.  A graph is generated with the abscissa  centered  vertically
     and  the  data points displayed as symbols.  The 'Residplt' command
     should always have the residuals  as  the  ordinate,  the  abscissa
     being any of the chemical concentrations or the observed calculated
     velocity.  Dashed lines are also graphed at plus or minus  the  95%
     confidence  t-statistic  times  the  residual  error.   This  flags
     outlying data points.

     [] RESIDPLT RESID .VS. CHEMCON
     [] RESIDPLT RES .VS. VELOC  (The observed velocity)
     [] RESID RES .VS. VCALC  (The calculated velocity)


          CALC command

     The 'CALC' command is similar to the 'FITPLOT' command and is  used
     when  more  than  one  chemical  concentration  is varying at once.
     'CALC' does not interpolate over the  chemical  concentrations  but
     rather   displays  the  calculated  velocity  at  the  experimental
     chemical concentrations and then connects these with line segments.

     [] CALC VEL. VS. CHEMCON
     [] CALC VEL .VS. CHEMCON. ERR. STDEV

PENNZYME user's document                                          Page 6
GRAPHICS COMMANDS


     1.3  Switches For The Graph-Type Commands

          SYMBOL switch


          Instead of representing data values as  discontinuities  in  a
     curve,  this switch allows the user to represent the data points as
     symbols.  Any keyboard  character  or  one  of  the  eight  special
     symbols  can be used.  All the points of the set or curve will have
     the same symbol.  This switch is  also  useful  for  modifying  the
     default  symbol value of the 'POINT' command.  A keyboard character
     will be used if it is  enclosed  by  single  quotes.   The  special
     symbols, square, diamond, etc.  are selected by using an integer in
     the range 1  through  8.   These  may  not  be  available  for  all
     installations.

     [] DRAW VEL .VS. CHEMCON/SYMB = '*'     use an asterisk
     [] POINT YVAR .VS. XVAR/SYMB = 2     use the second special symbol


          SIZE switch

     The 'SIZE' switch allows the  user  to  specify  the  size  of  the
     symbols  in  inches  if  these  are  present.   This is useful when
     displaying error bars since error bars are only  drawn  when  their
     vertical  dimension  exceeds  the vertical dimension of the symbol.
     Altering the size of the symbol allows control over the error  bars
     that are to be shown.

     [] FITPL VEL .VS. CHEMCON/SYM = 'X'/SIZE =  O.2


          SPACE switch


          The 'SPACE' switch allows the user to specify  the  amount  of
     space  left  araound  a  symbol.   This  prevents a connecting line
     segment from traversing the symbol.  This does not  stop  unrelated
     line  segments  from  traversing the symbol.  The space is given in
     inches.  This switch does  not  apply  to  commands  which  do  not
     connect the data values.

     [] DRAW YVAR .VS. XVAR/SYM=2/SPACE=0.2




     1.4  Data-Selection Commands


          There are currently three ways to select data to  be  graphed.
     All  three used the command specifier 'SELECT' and vary in the type
     of arguments expected.

PENNZYME user's document                                          Page 7
GRAPHICS COMMANDS


          The 'SELECT' command followed by the symbol '#' indicates that
     data  input  is  to  be  selected  by  line  number.  The lines are
     selected by expressions involving line numbers separated by commas,
     a  range  of  lines  specified  by  bounds,  and  a  range of lines
     specified by an inequality operator.

     [] SELECT #1-5     Selects lines 1 through 5
     [] SELECT #>6      Selects lines 7 through end of data
     [] SELECT #<20     Selects lines 1 through 19
     [] SELECT #1,2     Selects lines 1 and 2
     [] SELECT #1,2,6-9,11,>17  (The various modes can be mixed
     when separated by commas.)


          The 'SELECT' command followed by  a  variable  name  indicates
     that  data will be selected if it satisfies a constraint.  The only
     constraint currently  allowed  is  that  the  data  equal  a  value
     specified.   The  current implementation will only select the first
     contiguous set of data lines satisfying the constraint.

     [] SEL CHEMCON .EQ. 52     Select the line(s) where the
     variable CHEMCON has the value 52.


          The 'SELECT' command followed by the symbol '$' indicates that
     data  ranges will be selected according to predefined data subsets.
     These data sets cannot be defined within the graphics.   They  must
     be  defined  by a host system which allows the user to do this such
     as PENNZYME.  Several of the data subset indices can be used in the
     same SELECT command as long as they are separated by commas.

     [] SEL $2     Select Set number 2
     [] SEL $2,5   Select Sets 2 and 5


          PLOT command


          The 'PLOT' command is the last command entered and is used  to
     initiate the display of the graphics .  This should be entered once
     all the desired graph parameters have  been  set  for  the  current
     graph.   Output can be sent to a hard copy plotter by following the
     'PLOT' command with the word 'PLOTTER'.  Example [] PLOT =  PLOTTER
     Entering  a carriage return will erase the graph and allow the user
     to define a new graph.   The  previous  graph  may  be  redisplayed
     simply  by  entering  the 'PLOT' command again, if no Graph-type or
     Data-selection  commands  have  been  entered  since.   The   Setup
     commands  may  be  used to vary the layout of the graph.  Similarly
     when the graphics is used as an option within a host program,  upon
     reentering  the  graphics  the  last  graph  can  be regenerated by
     entering the 'PLOT' commands.  The new graph will then use the  new
     data  values if these have been modified by the host program.  With
     PENNZYME, one can display a quality of fit graph, exit the graphics
     and optimize the kinetic parameters, enter the graphics and display

PENNZYME user's document                                          Page 8
GRAPHICS COMMANDS


     the new quality of fit graph using the  optimum  kinetic  parameter
     values.


          QUIT command


          The QUIT command is used to exit from the graphics program.

PENNZYME user's document                                          Page 9
EXAMPLES OF GRAPHICS COMMANDS AND RESULTING GRAPHS


     2.0  EXAMPLES OF GRAPHICS COMMANDS AND RESULTING GRAPHS

     [] DRAW YVAR .VS. XVAR
     [] PLOT

      |
      |            /\
      |           /  \
      |          /    \       /\
      |         /      \     /  \
      |        /        \   /     \
      |       /          \ /       \
      | -----/                      \----
      |/
      |--------------------------------------------


     [] DRAW YVAR .VS. XVAR/SYM = O
     [] PLOT

      |
      |             O
      |            /\
      |           /  \          O
      |          /    \        / \                Use symbol O
      |         /      \      /   \               to denote point
      |        /        \    /     \
      | /O---O           \_O/       \
      |/
      |---------------------------------------------


                                                   
     [] DRAW YVAR .VS. XVAR
     [] POINT UVAR .VS. TVAR
     [] PLOT

      |
      |            /\                         Two different
      |           /  \                        sets of
      |          /    \  x    /\              variables      
      |         /       \    /  \             using different 
      |        /  x      \  /     \           representations 
      |x      /           \/       \  x       may be graphed
      | ------                      -----     simultaneously
      |  x
      |-------------------------------------

PENNZYME user's document                                         Page 10
EXAMPLES OF GRAPHICS COMMANDS AND RESULTING GRAPHS


     [] DRAW YVAR .VS. XVAR/SYM = O
     [] SELECT  1-3,5,6
     [] PLOT

      |
      |
      |                                        The select command
      |                     -O------O--        is used to include
      |   O-----O-        /                    or exclude data
      |  /        \--    /                     values from the
      | /            \-O-                      curve defined by
      |O                                       the preceding 
      |                                        graph-type command
      |--------------------------------------


     [] DRAW YVAR .VS. XVAR
     [] SELECT  1-3,5,6
     [] POINT UVAR .VS. TVAR
     [] PLOT

      |                                   The select command does
      |                                   not affect graph-type
      |                  x                commands which follow
      |                                   it
      |
      |          x
      |     -------         /
      |    /       \       /
      | x /         \   --/
      |  /            \/x          
      | / x                    
      |-----------------------------------


     [] DRAW CVAR .VS. DVAR                   The select command
     [] SELECT  1-5                           when used repeat-
     [] SELECT  6-10                          edly  generates 
     [] PLOT                                  distinct curves
                                              based on the values 
      |            /\                         set by the  preced- 
      |           /   \                       ing graph-type 
      |          / /\   \                     command.  This is
      |   ------/ /  \   \                    used to display 
      |  /       /    \   \                   families of curves
      | /  /----/      \    \                 if the data is 
      |/  /             \     \------         organized in that 
      |------------------------------------   fashion.

PENNZYME user's document                                         Page 11
EXAMPLES OF GRAPHICS COMMANDS AND RESULTING GRAPHS


     2.1  Graphics Commands Specific To PENNZYME

     [] FITPLOT VEL .VS. MGADP                Display observed
     [] SELECT  1-5                           velocities and
     [] PLOT                                  superimposed curve 
                                              calculated veloci-
      |                                       ties at interpola-
      |          O------O                     ted concentrations.
      |     O---/                             This only makes
      |  O /                                  sense if the first
      |  /-                                   variable is the
      | O/                                    velocity variable.
      |/                                       
      |-------------------------------------  


     [] FITPLOT VEL .VS. MGADP. ERR. STDEV     Displays error
     [] SELECT  1-5                            bars.  These are
     [] PLOT                                   drawn only if they
                                               exceed the size of
      |          -   -                         the symbol.
      |          |   O                         Vertical lines are
      |          O   -                         missing from error
      |      -   |                             bars because they
      |    - O   -/------                      cannot be repre-
      |    | - /                               sented by print 
      |   /O/--                                symbols. (The 
      |  / |                                   points do not fit 
      | /O -                                   the line so there
      |/                                       is room for the
      |--------------------------------------  error bars.)


     [] FITPLOT VEL .VS. MGADP
     [] SELECT  1-5
     [] SELECT  6-1O
     [] PLOT

      |                      O
      |                 O/-----
      |             -----
      |           O/
      |          --
      |         /            x               Multiple curves
      |       O/          /-----
      |       -       x---
      |      /    x---/
      |    O/  --/
      |    /   /
      |  /  /-x
      |O/-/
      |//x
      |---------------------------------------

PENNZYME user's document                                         Page 12
EXAMPLES OF GRAPHICS COMMANDS AND RESULTING GRAPHS


     [] CALC VEL .VS. MGADP
     [] SELECT  1-5
     [] PLOT

      |           O   ------               Displays calculated
      |          /---/                     velocities
      |        O/                          not interpolated
      |      -/                            over concentrations
      |     / 
      |    O/
      |   /
      | O/
      | /
      |--------------------------------




     [] RESIDPLT RESID .VS. MGADP
     [] PLOT

      | O
      |--------------------               Uses one symbol to
      |     O             O               denote data values
      |--------------------               of entire data.  This
      |                                   only makes sense if
      | O  O        O     O               the first variable
      |             O                     is the Resid variable.
      |--------------------
      |--------------------


     [] RESIDPLT RESID .VS. MGADP
     [] SELECT  1-5
     [] SELECT  6-1O
     [] PLOT

        O
      |----------------
      |     x      O     x                Uses a different
      |                                   symbol for each
      |           x                       data subset
      |--------------------
      |           O      O
      | x   O      
      |           x
      |---------------------
      |--------------------