How to Use Multi-Task DDT

	DDT is a symbolic assembly language level debugger for PDP11
which normally is included in a task image by specifying its name
on the input side of a taskbuild with the /DA switch to indicate that
it is a user debug aid. It allows one to examine code and see it, or
enter it as code, to enter symbols, and resolve addresses relative
to symbols. Thus, one normally needs only a map to use it, not
necessarily assembly listings. (One may predefine a short file with
global symbols and append it to the DDT symbol table and avoid even
the need to use a link map.)
	One pays for this power in memory; DDT may require as much as
6K of memory, which may not be available in a large task image. Even
the DEC debugger, ODT, which is a strictly octal debugger, requires
1K to 2K of task space. Thus it is comparatively frequent to have a
program too big to debug. That's unfortunate because the big programs
are usually the ones most needing to have a debug aid to help sort
out why they don't work.
	DDT22M (M for Multi-tasking, 22 for 22 bit addressing) is
a special task which includes a version of DDT and a control
program in one task, and a very short (about 150 words minimum, or
about 200 words for support of the ability to debug floating point
with examination and display of floating point contexts in floating
accumulators) "kernel" debugger in the task that is to be debugged.
It operates by going around some of the walls placed by the operating
system in RSX and IAS systems. In this scheme, DDT is able to examine
or modify the target task's address space directly, and controls
execution of the target by interaction with the kernel debugger. This
frees all examination and display functions from the target task's
address space and permits debug of all but the most pathologically
huge programs. (DDT can perform examines/deposits in a task by self-
mapping as described above, or by a pure mode as below that is not
sensitive to task motion in memory.)
	The DDT system may, if desired, be assembled to permit access
to the target task via sends and receives (executing MOV or MOVB
instructions in the target's context) to allow access to the
target's space without dependence on physical memory locations
and without sensitivity to swapping/shuffling activity. The
variable SR.CTL will control this; set it nonzero to use mapping
via send-data/receive-data, zero to use the DDT internal pseudo
mapping. This method is safer than the "pure DDT mapping" mode
above, but is notably slower (by a factor of 3 more or less). This
is not important for execution from one breakpoint to another,
but single stepping is slower. Single stepping is used for memory
watchpoints too. Thus, DDT mapping mode should be turned on
in those cases unless the system is swapping heavily.
	To generate the system, DDT22 must be assembled with the
parameter MU$DBG defined, and linked with DDTMU. The task name must
be DDT22M, so only one such task may exist at a time. The DDT22M task
is normally built with floating point support too if the machine
has FPP instructions (or the Floating Point Emulator available on
DECUS RSX SIG tapes for RSX11M or IAS). This permits examination or
modification of memory in Floating Point format. The debug kernel
may be assembled with $D$FPU defined if the target task's floating
accumulators are to be available to the debugger.
	The debug kernel DDTKNL must be assembled, with or without
$D$FPU defined, to link into the target task.
	There is a command file DDTBLD.CMD which builds a suitable
DDT and the debug kernel.
	NOTE: if using RSX11M+, define K$ID when assembling
DDT22, and if using either RSX11M or RSX11M+, it is desirable
to define R$XMDB and assemble with [1,1]EXEMC/ML when assembling
DDT22, and with only the definition when assembling DDTMU. The
file DDTPRM should be used and edited for your system.
	DDT22M is linked with DDTMU and DDT22/DA as its main
inputs. The target task is linked with DDTKNL/DA as an input
file. Given these preparations, you are ready to debug your
code. Note that DDTKNL will trap all odd address traps,
illegal instructions, segmentation errors, and breakpoints.
It, AND DDT22, must be edited to handle non-RSX EMT or TRAP
instructions.  (See the source; such changes are not recommended.)
Be sure to use the /FP switch in taskbuild if your DDTKNL has
$D$FPU defined.
	Now install DDT22M or use a command like

RUN DDT22M/TASK=DDT22M

to run the task with the required task name DDT22M. The DDT task will
announce its presence and sit there. Type $G ($ means "escape" hereafter
and may be eaten by the terminal for some terminals (like LA120, VT100,
VT52) but will still work even though it does not echo. This starts
the DDT22M task up and leaves the terminal free. DDT may be built to
issue its own $G optionally. If it is, you need type nothing. However,
be SURE that the task name is right. Normally it will be DDT22M, but
the code in DDTKNL determines what the name MUST be. DDTKNL MUST know
the task name of your debugger, and the debugger must be active before
your task starts.
Note: IAS users must install DDT22M; the /TASK= switch fails there.
	Now you may start your target task in whatever way you like.
When your target task comes in, DDT will be re-activated. If you
built with R$XMDB defined, DDT is automatically mapped to your
task at every message from it (which permits use of one copy of
DDT22M for several tasks; the RCVBUF area has the RAD50 task name
in its start. DDT will print the task name you are examining and
keep breakpoints straight for many tasks.)
	The DDT22M task may map with either of 2 address spaces
now. Initially it is in its own space. To allow examination
of the target's space, type the $UM command. To return to the
DDT space, type $UV. (Remember "$"="escape", not just dollar sign.)
Normal procedure is to type $UM, then set breakpoints (or single
step mode), then type $G first to start your program. You MUST
use the $UM command before beginning the target task if any breakpoints
are to be set.
	When you hit a breakpoint, DDT symbols R0 through R5, SP,
PC, and U.PSW are the target's registers, and DDT symbols AC0 thru
AC5 and FPSTAT are the target's floating accumulators if DDTKNL
had floating support. These may be examined as you would under
normal DDT. To examine DDT's registers, you must use the $UV
command and examine D.R0 thru D.R5, D.SP, and D.PC. Remember to
use the $UM command before proceeding. The normal $P command will
proceed from breaks normally. Single stepping may be done when
not in $UM mode, but this is not recommended since you could forget
what you're looking at. Symbol U.DSW is the task's $DSW at the
breakpoint also.
	Once in DDT you may at any time get DDT to exit by typing ^Z or
BYE$G. However, if your target task exits (normally or otherwise)
DDT22M won't know. Normal action is to abort DDT22M from the console
when done with it. The command to do this is

ABO DDT22M

which will end the session. (There is a hook in DDTMU and DDTKNL that
permits you to install a task that will send an exit message to DDT22M
to get it to exit; see the source if you don't care to abort DDT22M.
	Almost all DDT commands work in this system. Even the i$X command
works, executing instructions in the target's context.
Also, once you type the initial $G to DDT22M when it first starts,
all subsequent $G or $P commands are interpreted as target addresses,
and the DDT22M task itself is in an idle loop awaiting intertask messages
from the target.

	APPENDIX

	The DDT22M sources have been modified so that if $$SDT is defined
in DDTMU, a "system" debugger results. This debugger will type the
task name out whenever a new task is seen to have sent a message to DDT
and will save and restore the breakpoint information by task name
for several tasks, automatically inserting the correct values for DDT
to use with each breakpoint entry from a DDTKNL module. Thus, the user
knows at all times which task he is talking to, and may control several tasks.
It has further been provided that a task restart will reinitialize
breakpoints, so that DDT22M may be left running, with symbols defined,
across several runs of a task. This may be more convenient than having to
re-enter symbolic locations every run.
	Memory watchpoints as well as breakpoints are remembered on a per
task basis and the address of a watchpoint at a break will be shown.
	DDT now has the capacity to  read symbol table files and look
up symbols. This capacity exists in all RSX/IAS DDT versions but is most
recommended for the system debugger since it has more address space. The
$UO and $UQ commands open and close the symbol table file; the $UO
will prompt and use a GCML$ call to read the lun. A side effect of defining
SM$FIL to allow this is that the luns .ODTL1 and .ODTL2 are used by DDT
for I/O. .ODTL1 is used for the terminal and .ODTL2 is used for the .STB
file. These luns are added by TKB whenever a debug aid is included.
	Also added is the $UZ command to allow memory modification
breakpoints. These are simulated by infinite single stepping and break
when any of up to 8 addresses' contents change. The logic is simple minded
and does not really tell what changed. However, a simple application would be
to monitor $SEQC for a program from F4P to allow a single-statement
breakpoint. It is slow, but needs no compiler modification.
There is also a preprocessor that can make a faked up .STB file from
FORTRAN listings and maps and allow DDT to know all line numbers,
statement labels, and variable names in the FORTRAN program. There
is also some support for a breakpoint at $ALBP2 to avoid having DDT
reset any instructions in the wrong overlay. This allows one to
monitor overlays and insert breaks for new overlays at the time of
overlay load.
	The $UK and $UU commands are extended so $1UK loads KNL I APRs and
simple $UK loads KNL D APRs. $UU is not normally so modified (it's an
assembly conditional) but if K$ID is defined, the kernel mod is generally
there. A bit of protection against access attempts to nonexistent memory
is available if the symbol MAXBK is defined as the highest legal 32 word
block in the machine. It defaults to 256KW (20000 octal) but may be set anywhere.
DDT will simply not do any access if APRs are found invalid. DDT is not
totally infallible in this calculation, and it will give no error
indication, but at least it should not crash or access invalid regions
very much.
	The DDT Symbol Table File Reader will cache its symbols (LRU) in the
normal symbol table, in a special area. This should reduce file accesses
reasonably. When changing tasks to debug, the normal procedure will be to
open a new .STB file as needed. However, due to the caching, this may not be
necessary after the first time; experiment. You may want to go into the source
and enlarge the cache too, or possibly shrink it. Cached symbols may be killed
as any others, but beware of this. They normally are "held" in the table as
nonzero but small values to prevent the space from being used for normal
symbols. A killed symbol may be re-used by console definition of a new
symbol and then be overwritten by the .STB cache logic if any cached
cells are removed. The 1$UO logic will erase the cache, though, while
the $UQ logic will not.
	Be aware that DDT does not change symbol table files automatically.
If you are debugging several tasks, you should change .STB files yourself
where you need to, possibly clearing the cache of symbols to avoid
confusion.
	To minimize the resources needed for DDT's intertask communication,
DDT will normally send messages to tasks sending DDT messages, but the
tasks will, in DDTKNL, receive and send messages only to DDT22M, thus
leaving othes queued. Also, a generation option allows ASTs to be
disabled during breakpoints (when DDTKNL may reasonably expect
messages from DDT) so thatno message-in ASTs will be activated
elsewhere. The ASTs are re-activated upon dequeue of a message from
DDT. Note that if ASTs were disabled on entry to a break, though, they
will not be reenabled by DDTKNL. This slightly enlarges the DDTKNL
task, but for system-wide debug is so useful as to be mandatory for
avoidance of interference with intertask communication in the application
being debugged.
	There is nevertheless an effect that DDTKNL will have on communication
not directed to it. Once a message AST is queued to the target task due to
a DDT message, that AST is not removed from the task by the system, even
though DDTKNL has read the data packet. Therefore it is necessary for a task
that is receiving message ASTs to ensure there is really data present for
it to act on before doing anything else. It is evidently necessary also
for the task to  continue attempting to receive data until there is an
error. A simple attempt to read data and use it based on the existence of
an AST will become erroneous if DDTKNL is included. However, a well designed
system will have a check that will prevent damage.
	Multiple versions of DDT22M may be made up with different task names.
Only DDTKNL.MAC and DDTMU.MAC need be edited, and the DDT22M literal task
names in SDAT$ and RCVD$ macros replaced by some other task name, which
must be the name of the debugger used with that pair of tasks. Actually,
DDTMU need not, I think, be altered, but DDTKNL will expect to know the
task name it is talking to and will always need to be altered.
	A note to remenber: the memory break points (or "watchpoints") are
really not designed to be used for several tasks at a time. You may use them,
and they are replicated on a per task basis as are breakpoints, but
since they are handled via single stepping, it should be recalled that
it is VERY EXPENSIVE in CPU time to have watchpoints active and it
is highly recommended that they be used for at most one task at a time.
	The DDT variable U.DSW will normally contain the contents of
$DSW at a break and may be located automatically by that name. The
variable $DSW is the value of $DSW in the DDT22M task context, which
is not normally very meaningful. A consideration to be added possbly
at some time in DDT is a mode flag to go with each variable to indicate
which virtual map it corresponds to. The expectation is that normally
DDT22M will be left in $UM mode and variables local to DDT (like JOBSA)
will seldom be accessed. Once DDT22M is started, one may query PC
to find where a task is while still in $UM mode; only the initial
startup lacks this.
	DDT may be built to support conditional breakpoints. If these
are enabled, the arrays D.BMSK and D.BTST are important. They are
word arrays. If the word in D.BMSK corresponding to the breakpoint
number (e.g., B0 is D.BMSK, B1 is D.BMSK+2) is nonzero, THEN the
word at the location DDT will open at the break will be ANDed with
that D.BMSK element. If the result is different from the value
in D.BTST, the break will be ignored.
	Where DDT is communicating with another task, 14 RSX directives
are required per breakpoint/proceed pair plus breakpoint open overhead.
This is done by DDT without help from RSX where exclusive use of
send/receive directives is not in use. If these directives are in
exclusive use, some 16 additional RSX directives (minimum!) are
executed with each breakpoint (8 to restore the original instruction
at the break, 8 to put back the BPT at the proceed). Because of this
overhead, it is desirable to allow DDT to do its own mapping where
it is feasible. However, in a loaded system, it is probably best
to allow DDT to use send/receive always, run slowly, and be SURE
no shuffling takes place DDT dowsn't know about. DDT may be assembled
then to not actually try to reference any I/O page locations if
that is desired.