Addenda for TECO Version 28



     The TECO m
anual in this kit describes TECO version 27;   the
TECO  in  the  kit is versio
n 28.  TECO version 28 is totally up-
wards compatible with version 27 and has 
the following  new  fea-
tures:


Colon Modifiers for Xq and ^Uq Commands


     The two commands that load text strings into Q-registers (Xq
and  ^Uq)  m
ay be preceded by a colon modifier.  This causes them
to append the text to the
 original contents  of  the  Q-register,
rather  than overwriting it.  For exam
ple, assume that Q-register
A contains the string

                          
     ABC

and the buffer contains the string

                              
 DEF

Then executing either the command

                              :HXA

                               or
                            :^UADEF$

will
 cause Q-register A to contain the string

                             ABCDEF



Character Group Search Modifier

     In a search string, the search mod
ifier ^EGq matches any one
of  the  characters  contained  in Q-register q.  Fo
r example, if
Q-register A contains the string

                             
  JKL

then the search string

                             X^EGAY

will m
atch any of the following strings:

                               XJY
      
                         XKY
                               XLY



           
                                                PAGE 2



Use of EI$ in TECO
.TEC (RSX-11 TECO only)

     If an EI$ command (to close the indirect  comman
d  file)  is
executed during the processing of a user's TECO.TEC startup file,

the final MY$$ which causes processing of the command line is not
executed.   
This results from the fact that the MY$$ normally ap-
pears in TECO's type in a
fter all command files  have  been  pro-
cessed.   Executing the EI$ command ca
uses all "type ahead" to be
discarded to allow a TECO command file to prompt an
d  read  input
from  the  terminal  (and not read extraneous type ahead).  It i
s
assumed that a TECO startup file  that  executes  EI$  and  reads
input  fro
m  the  terminal will want to manage the rest of TECO's
startup.  If it still w
ants to process the command line, it  must
issue the MY itself.