The following describes the enhancements we have made to the RSX11M
operating system which were originally added under V3.0 and have since been
modified to work under V3.1.  Most of the corrections are in SLP file format.
I am sorry the documentation file is not in RNO format but I created this
document from an non-RNO documentation system.  The name of the files that 
implement each described enhancement preceed its description.  The software
is provided as-is, and no support is implied although it has been running
with no problems on numerous RSX11M systems at NASA/Ames and is supported
internally by our RSX11M support group.  The SLP files will also include 
most of the software dispatch patches for that module through NOV 78.  If
there are questions I can be reached at (415) 965-5935 during the afternoons 
and usually the evenings.    All the .TSK files included are built non-
privileged for mapped systems and probably are directly useable.

				Greg Thompson
 
 
                         NASA/Ames RSX11M System Enhancements
 
        The following enhancements have been made        Revised: 11/07/78 
        to the  RSX11M V3.1  operating system:           By: Greg Thompson 
 
        TTDRV.COR
 
             Auto baud support is in for DH11 lines at 300, 1200 and 2400
             baud.   The universal speed character is ctrl-c.  (You can't
             go 2400 through the digital switch though.)   The  auto baud
             table are at the very start of the TT driver  code  and  are
             set up to allow the use of  any  single character  auto baud
             algorithm.
 
             Ctrl/o  (flush  output)  will  break  out of ctrl/s (suspend
             output) mode. 
         
             The Clear to send (CTS) line is ignored for DH11/DM11 lines.
             Since  TRAN  loops  Request  To  Send (RTS) back to CTS this
             generates  another  interupt  when the PDP tries to drop the
             line  (by  dropping RTS and DTR) at which time the old ttdrv
             code  brought  up  RTS  and DTR causing another interupt and
             causing  the  switch  to  sometime  hang  the line (since it
             didn't  see  DTR  drop long  enough).  Ignoring CTS seems to
             fix the  problem.  (TRAN is our EIA RS232 intra-base high 
             speed time-division multiplexing communication system.) 
         
             The  ring  line is now ignored after the connect sequence is
             completed  and  the  carrier  line  is  high.   This  is  in
             accordance  with the EIA standards and fixes a bug in the TT
             driver support of remote terminals. 
         
             There  is a hardware problem with DL11-A terminal interfaces
             which manifests itself my dropping its input interupt enable
             bit.   To  help  alleviate  this  problem the input interupt
             enable bit is set anytime anything is written to or received
             from the device.
         
             The lower-case flag and buffer size are now not reset when a
             DH11 line connects. 
         
             Control-Y will abort the task which currently has I/O active
             to the terminal.  Input is first terminated with a Ctrl-Z.
         
        BROAD.COR
             
             The ALL: and LOG: parameters on the BRO command are now non-
             privileged and now includes terminals that have the terminal
             attribute in the UCB.   Also  BRO to not logged-in terminals
             is allowed. 
 
        DREIF.COR
         
             Allows negative abort codes which indicate no abort messages
             are to be written out.  Used in implementing Control-Y key. 
         
        REQSB.COR
 
             Higher  priority  tasks  which can not fit in memory will no
             longer  prevent  lower  priority  tasks  which  can fit from
             running.
 
        SYSOV.COR
 
             CLQ is now non-privleged. 
 
        TASOV.COR
 
             TAS now has an optional taskname parameter. 
 
        SPROV.COR
        SDSOV.COR
         
             The slash "/" is optional on SET's keywords.
         
             The  SET  /UIC=[x,y]  command  for privileged users will not
             change  their  logged-in  UIC anymore.  It will still change
             their  default  UIC.   This is so a WHO command can identify
             users using their logged-in UIC.  It doesn't appear to cause
             any problems. 
         
             There are five new options on the SET command.   LOGGED-OUT,
             OFFLINE,  ABSCAN (Expecting a speed character), DISABLED and
             CARRIER-WAIT.  Used without an equals  sign  they  present a
             list of terminals that have or do  not  have  the  specified
             mode  set.   All  but  CARRIER-WAIT when used (by privileged
             terminals) with an equals sign and a device name they set or
             clear these modes.
         
        MCRDIS.COR 
        MC2.MAC
        INSPS.COR
        INSFL.COR
        INSLB.COR
         
             The restriction of only one activation of any given task per
             terminal  has  been  removed.   You no longer will get  Task
             Active error messages.
         
             LOG  is  now  allowed  in  addition  to  HEL for logging-in.
 
             If  MCR  receives  a  command  for  which it can not find an
             installed  task  that  handles  it and if the ...MC2 task is
             installed  then  MC2 will pass the command line to this task
             and   request  the  task  to  run.   The  auxillary  command
             dispatcher task  ...MC2  first checks to see if it is one of
             the commands processed internally.  These commands are: 
         
             DIRectory <filespecs> - equivalent to "PIP <filespecs>/LI". 
        	        	  Switches /BR, /FU and /TB are allowed. 
         
             DELete <filespecs> - equivalent to "PIP <filespecs>/DE".
        	        	  Version numbers are required.
             
             ERAse <filespecs>  - equivalent to "PIP <filespecs>/DE".
        	        	  Version numbers are optional.
        	        	  If omitted all versions will be deleted. 
         
             FREe <device>      - equivalent to "PIP <device>/FR". 
        	        	  <device> is optional.
         
             PURge <filespecs>  - equivalent to "PIP <filespecs>/PU".
         
             REName <new>=<old> - same as "PIP <new>=<old>/RE".
         
             SPOol <filespecs>  - same as "PIP <filespecs>/SP".
         
             TYPe <filespecs>   - same as "PIP TI:=<filespecs>". 
         
             UIC <grp,mem>      - same as "SET /UIC=[grp,mem]".
        	        	  Example:  UIC 6,6   Current setting
        	        	  displayed if no parameter specified.           
             
                If  the  command is non of the above then ...MC2 looks in
             CM:[1,55] for a .TSK or .CMD to process the command.  If the
             user  is  a  privileged  user  the  CM:[1,56]  directory  is
             examined.   If  no  file is found the search is continued in
             the  users directory (SY:[grp,mem]).  If ...MC2 still has no
             success  then a "MC2 -- Command not found." error message is
             returned  to  the user.  If a .CMD file is found then ...AT.
             is  envoked.   If  a  .TSK  file  is  found then the task is
             installed, marked for removal on exit, and invoked using the
             original  command  line  ...MC2  received.   This  mechanism
             allows  just  the  tasks in most frequent use to be normally
             installed  and  other  tasks  to be installed when necessary
             thus conserving pool space. 
   
             Also   the  following  commands  have  been  implemented  by
             indirect command files in CM:[1,55]:
               
             PRO <filespecs>    - sets the file(s) protection bits to
        	        	  [R,R,R,R] (read-only) for everyone.
        	        	  Uses:  "PIP <filespec>/PR:167356"
             
             UPR <filespec>     - resets file protection bits to the 
                                  system default of [RWED,RWED,RWED,R] 
                                  which is system, owner, group have 
                                  full access, others read-only. 
             
             CRT                - Issues a "SET /CRT=TI:" to enable CRT
                                  type character deleting. 
             
             LOWER              - Issues a "SET /LOWER=TI:" to enable
        	        	  lower case input and output. 
             
        INDERR.COR, INDFDC.COR, INDNP1.COR, INDOPN.COR, INDMCR.COR,
        INDROT.COR, MGCML.COR
 
             The  MCR  indirect  command  processor  IND,  now allows the
             passing  of  parameters  from  the command line.  The global
             string  variables  $P0,  $P1, ...  $P9 represent the command
             line  parameters  which  must  be  seperated  by one or more
             spaces.   $P0  represents  the name of the file that envoked
             IND.   $P1  is  really  the  first  parameter.   Remember to
             .ENABLE   SUBSTITUTION  before  you  try  to  use  them  for
             substitution  and  to .ENABLE GLOBAL before you try to .SETS
             them.   Only  as  many of these variables will be defined as
             there  are parameters for them.  You can use .IFNDF or .IFDF
             to  determine whether or not any given parameter is defined.
             To  use  the  IND  switches  /TR, /DE, or /NOMCR supply them
             immediately  after  the file name with no space between them
             and the file name.  Example: >DOIT/NOMCR FOO BAR
         
             IND  also  has  new .ENABLE/.DISABLE options.  One is called
             SILENT  and  disables the displaying of MCR commands.  Since
             IND  can  no longer wait for the command prompt ">" from MCR
             after  the  command  has  completed,  MCR commands should be
             followed  by  a .WAIT on the task that processes the command
             if  the  silent mode is enabled.  For example a "DIR [1,24]"
             command  in a MCR command file should be followed by a .WAIT
             PIP  when  the SILENT mode is enabled.  The other new option
             is PROMPT which disables or re-enables the displaying of the
             MCR  ">"  prompt  after  the IND task exits.  This is useful
             when you want an command file to issue a RUN on another task
             and  exit  and  you  don't  want an command prompt to appear
             until the RUNed task exits. 
         
        ACNTLG.TSK, ACNTLG.MAC 
         
             This  task  processes  login  accounting  messages  from the
             ...HEL,  ...BYE  and RSTLOG tasks and reports the logging in
             and out and system restarts to the file  LG:[1,2]ACOUNT.LOG.
   
        RSTLOG.TSK, RSTLOG.MAC 
 
             This    task    should    be    run    during   startup   in
             LB:[1,2]STARTUP.CMD  so that system restarts are recorded in
             the account logging file. 
 
  	HELLO.COR 
 
             If  the  ACNTLG  task  is installed ...HEL reports the login
             (via  send-data)  to  the ACNTLG task who then records it in
             the account logging file. 
 
             A  message telling the user that he has mail is displayed if
             mail is found for him in the mail directory. The user should
             then issue the MAIL command to deliver his mail.
 
             The user's LOGIN.CMD file is executed without displaying the
             "@LOGIN.CMD" message. 
         
        BYE.COR
 
             If  the  ACNTLG task is installed ...BYE reports the logging
             out to it.
 
             In addition to nonprivileged tasks bye will abort privileged
             tasks whose names are in a table internal to BYE.  Currently
             CON and RMD are aborted by bye. 
 
        ALTOV.COR
 
             The  bug  involving  ALTing  tasks with one or two character
             tasknames has been corrected. 
 
        TKTN.COR 
 
             The bug in the queue flushing code has been fixed  and  TKTN
             now  always uses  IO.WBT  to output messages,  preventing it
             from hanging ...MCR up when it tries to output to a terminal
             that is currently inputing. 
 
        WHO.MAC 
 
             The new command WHO is used to display who  is  logged  into
             the system.  The command displays the terminal number logged
             into, his UIC,  last and first names,  and the time at which
             the user logged in.  All task names which are active for the
             user are displayed on the next line.
         
        CON.TSK, TELNET.TSK, RTDRV.MAC, RTMANUAL.DOC 
         
             This  software implements a virtual terminal connection from
             one RSX11M computer to another over DECNET V1.2.   A version
             for DECNET V2 is currently being developed. 
         
        ECO.TSK, ECO.MAC 
         
             This task simply echos to the terminal its MCR command line.
         
        ATT.TSK, ATT.MAC  (From Dan McCoy) 
 
             This task takes as its only parameter a filename and permits
             the  issuer to alter the record (carriage control) attribute
             of the file.  Switches are: 
       
                /CR     Give the file the carriage control attribute.
                        When the file is printed on a record oriented
                        device (ie a terminal or line printer), a
                        line feed is printed before each line and a
                        carriage return is printed after each line.
                        This switch is the default if no switch is 
                        specified. 
 
                /FT     Gives the file the Fortran attribute.
                        When the file is printed on a record oriented
                        device, the first character of each line is
                        interpreted as a Fortran carriage control
                        character. 
 
                /-FT    Same effect as /CR 
 
                /-CR    Gives the file no carriage control attribute.
                        When the file is printed on a record oriented
                        device, no carriage control is added to the
                        output;  internal carriage control assumed.
 
        HELP.TXT 
         
             A  tree structured help file for obtaining information about
             commands and features of RSX11M.
         
        PSDRV.MAC
         
             Revision  H  of  PSDRV  fixes the problem of ABOrting a task
             using  the  picture  system.   The  old PSDRV did nothing at
             cancel entry of the driver.  The cancel entry is called when
             a  task is aborted which has a LUN (attached) to the device.
             This  problem would show up as a task sitting in I/O rundown
             (RDN)  with  the marked for abort bit (ABO) and (HLT) on but
             not  being  able to abort the the task essently knocking out
             the  tasks  memory  until  a  restart.   This was especially
             annoing  to  fortran  users  since  fortran  aborts the task
             automatically  when  any  error  occurs.   The  problem  was
             basically  that  in  aborting,  the  PSFIN  function was not
             occuring.   Thus  decrementing  the  I/O  count and clearing
             various  PSDRV  variables  was  not occuring on aborts.  The
             cancel entry code thus basically does a PSFIN for you.  Note
             that  a  normal task exit also causes the cancel entry to be
             called therefore a PICSYS user can now leave out the CALL to
             PSFIN  and  not  do  himself in (although for compatibility,
             etc.  I would recommend that you leave the calls in.) 
 
        LPDRV.COR
 
             The  line  printer  driver  is  now  smarter in that it will
             ignore extra form feeds if it knows it already just output a
             form  feed  thus  eliminating the extra pages that the print
             spooler  waists.  Unfortunately you can still fake it out if
             you  use  the advance button instead of the form feed button
             to  advance  the paper after a listing is completed.  Please
             use form feed button to advance  paper for now. 
 
             The  line  printer  driver  also supports an IO.WAL function
             which  allows  a  task to use the plotting features of a DEC
             LV11 plotter/printer. 
 
 
        The following programs obtained from a previous DECUS tape,  were
        enhanced:
 
        MAIL.TSK, MAIL.MAC      MAIL [user name or uic]
 
             If issued with no parameters it delivers the users mail else
             it  prompts  for the user to enter mail to send to the given
             userid.  End input with a ctrl-z.  After delivering the mail
             the user is asked whether he wants to delete the mail,  save
             it  by  renaming  it  to the users directory or retain it by
             leaving  it  in  LB:[10,3] to be delivered again by the next
             MAIL command.  If the rename is unsucessful because the user
             does not have a directory on the LB: disk the mail is simply
             retained. 
 
        FRG.TSK, FRG.MAC        FRG ddu: 
 
             Displays disk fragmentation characteristics.
             It was changed to use double precision arithmetic.
             The error messages were enhanced. 
             It now allows unit number zero as a default.
             A size of the largest free block is displayed.
             Output is now in lowercase. 
             The hole ranges were altered to a more logrithmic scale.
             Allowed the non-privileged user to use it.
             And it was built /PR:0 since it doesn't reference the EXEC. 
 

         CMTMO.COR fixes a bug found in DECNET V1.2
              
         P.S. You can create the needed logical devices CM: and LG:
              by doing a global ASN in VMR.