CCL -- Console Command Language
                             RSX11M V3.2
                             User's Guide
                              15-MAR-79



          The normal user interface to an RSX11M operating  system  is
     via  MCR  (Monitor  Console  Routine).   If terminal input is not
     specifically requested by a task, all data, or commands typed  in
     at  a  user's terminal are sent by the terminal driver to MCR for
     decoding.  The MCR task (and its child ...SYS) decode  user  com-
     mands(ACT,  ABORT, RUN, DEV, etc.).  Tasks installed with special
     names of the form ...XYZ are treated as a external  MCR  command.
     Hence if a user types 
      
     			XYZ commandline
      
     the 'commandline' in its entirity(or at least up to 76 characters
     is  sent  as  input to the task ...xyz.  this is the conventional
     way of supplying most system commands and controling  the  opera-
     tion  of  the  RSX11M  utility programs.  The limitations of this
     method are that each task must be installed to be treated  as  an
     external  MCR  command, and each extra installed task, uses valu-
     able pool space.  Moreover, because installed tasks use a  criti-
     cal  system  resource(pool),  only privleged users are allowed to
     install and remove tasks from the system.   The  normal  user  is
     restricted  to  starting tasks via the RUN command or using those
     tasks already installed.

          To alleviate this problem a user tailorable Console  Command
     Language  (CCL)  has  been  implemented which allows each user to
     have a private task control  language  which  will  pass  command
     lines  to tasks which are not installed in the system as external
     MCR commands.  When a user types in a command line, MCR is  given
     first  crack  at decoding it.  If MCR does not recognize the com-
     mand(first 3 letters) as either an internal( like  SET  /UIC)  or
     external  command,  then the command line in its entirity is sent
     to a task ...CCL, the Console Command Language task.  CCL in turn
     checks to see if it can find the command(the command stops at the
     first space, comma, =, <, or carriage return encountered).  First
     it looks in a user file USERCCL.CCL to see if the command is pre-
     sent.  If it isn't, it checks in file LB:[1,5]SYSCCL.CCL  to  see
     if  the  command  is a system CCL command.  If the command is not
     found anywhere, a warning message is printed.

          Each user may have an  individual  CCL  (USERCCL.CCL)  file.
     Instructions on how to structure a CCL file and some worked exam-
     ples are in APPENDIX A.  In APPENDIX B passing a command line  to
     a task via the RUN command is discussed.



                                                                PAGE 2



                         SYSTEM CCL COMMANDS



          A wealth of CCL commands exist to  simplify  the  amount  of
     type  in  a  user  has to do, and to allow the user access to the
     wide variety of RSX utility programs which  are  not  perminently
     installed in the system.

          In addition a number of commonly  used  commands  are  built
     into  CCL.   The  commands BRIEF, DELETE, DIRECTORY, LIST, PURGE,
     SPOOL, and TRUNCATE are internally decoded by  CCL  as  PIP  com-
     mands.  The command syntax for all of these commands is,
     		COMMAND  [filespec] [,filespec] ...
      
     The commands DIR and BRIEF do not require a  filespecifier.   All
     the  other  commands  require  a  file  or files to be specified.
     These commands have the following PIP equivalents.
      
     BRI[EF]    filespec		PIP [filspec]/BR
     DEL[ETE]   filespec		PIP filespec/DE
     DIR[ECTORY	[filespec]		PIP [filespec]/LI
     LIS[T]	filespec		PIP TI:=filespec
     PUR[GE]	filespec		PIP filespec/PU
     SPO[OL]	filespec		PIP filespec/SP
     TRU[NCATE]	filespec		PIP filespec/TR
      
     All other CCL commands are decoded from the CCL user  and  system
     files.

     TERMINAL CONTROL COMMANDS
      
     	CCL COMMAND			MCR COMMAND

          HOLD				SET /HOLD=TI:
          NOHOLD			SET /NOHOLD=TI:
          PAGE				Erases the terminal screen
          SHOW				@LB:[1,2]SHOW.CMD
          UIC				SET /UIC
          UIC   [G,M]			SET /UIC=[G,M]
          UIC = [G,M]			SET /UIC=[G,M]


     DIRECTORY COMMANDS

           
          /TB				PIP /TB
           
          FREE dev:			PIP dev:/FR


     FILE CONTROL COMMANDS

          COPY infile, outfile		PIP outfile=infile



                                                                PAGE 3



     SYSTEM UTILITIES
      
          Note:	Command lines for utilities started by CCL are
     		limited to 40-50 characters.

      
     ACCLOG			RUN $ACCLOG
      
     ACNT			RUN $ACNT
      
     BASIC			BASIC
      
     BCK			RUN DK1:$RMSBCK
      
     CHKSUM filespec		PAT NL:=filespec/CS,filespec
      
     CDA dev:=MM0:/SW		CDA dev:=MM0:/SW,LB:[1,54]RSX11M.STB/STB
      
     COMPRESS filespec		LBR filespec/CO=filespec
      
     CMP command line		Identical to CMP syntax
     COMPARE command line	Identical to CMP syntax
      
     CVL command line		Identical to CVL syntax
      
     DATEL			RUN $DATEL
      
     DIOP			RUN $DIOP
      
     DMP command line		Identical to DMP syntax
     DUMP command line		    "      "
      
     DSP			RUN DK1:$RMSDSP
      
     EXTRACT filespec,library	LBR filespec=library/EX:filespec
      
     FLX command line		Identical to FLX syntax
      
     FRG dev:			Identical to FRG syntax
     FRAG dev:			     "    "     "      "
      
     FTB commandline		Identical to FTB syntax
      
     LBR commandline		Identical to LBR syntax
      
     LST commandline		Identical to LST syntax
      
     PAT commandline		Identical to PAT syntax
      
     RECOVER filespec		Use RECOVER syntax
      
     REPLACE library,object	LBR library/RP=object
      
     RNO commandline		Identical to RNO format.
      
     RST			RUN DK1:$RMSRST
      
     SLP @commandfile.slp			Identical to SLP syntax
      
     SUBMIT GRP/MEM/PASWRD cmdfile



                                                                PAGE 4



     SUB GRP/MEM/PSWRD CMD	Identical to SUBMIT syntax
      
      
     VFY commandline		Identical to VFY syntax
      
     VMR			Identical to VMR syntax
      
     ZAP			Identical to ZAP syntax


     PRIVLEGED SYSTEM COMMANDS


       ACS DEV:/BLKS=N		Identical to MCR
       DISKSAVE			@LB:[1,2]DISKSAVE -- Returns user to
       				original disk and UIC when done.
       ERF			Identical to MCR
       ERRORS output,cmdline	@LB:[1,6]ERROR
       LOA(D) DEV:		LOA DEV:/PAR=DRVPAR
       MOU(NT)			Identical to MCR
       PSE			Identical to MCR
       SHUTUP			@LB:[1,2]SHUTDOWN
       SPQ			Identical to MCR
       SYE			Identical to MCR
       UFD dev:[UIC]		Identical to MCR
       UNL(OAD) DEV:		Identical to MCR



                                                                PAGE 5



                              APPENDIX A


                       CCL COMMAND FILE FORMAT


          The CCL command file has a  rigid  format,  some  fields  of
     which  were  intended  to be used but which have been lost in the
     mists of time.  A command specification consists of a  number  of
     keyword lines, followed by a number of parameter lines and final-
     ly by an action or skeleton command line.  There  are  of  course
     exceptions.  If the keyword is not found and its last characteris
     "?" then the command "?  keyword" is tried.  Thus help?   can  be
     made  to  list  the  names  of  all subjects on which help can be
     found, while file?  gives "HELP FILE".

          The command keywords are matched to 8 characters and parame-
     ters  may  be  up  to 30 characters each.  If a request for a re-
     quired parameter is answered by CTRL/Z then the program  abandons
     the command.
      
     EXAMPLE:
      
     	$1111M
     	$2811ASSEMBLE
     	?1Filename
     	*MAC %1%=[1,1]exemc/ml,[11,10]rsxmc/pa:1,[12,10]%1%
     	$1411TYPE
     	$2411LIST
     	?1File
     	*PIP TI:=%1.MAC%%2,.MAC%%3,.MAC%
     	$2822COMPARE
     	?1Files
     	?2Output
     	*CMP %2.SLP%/SL=%1;-1%,%1;0%
      

          The commands " M file " and "ASSEMBLE FILE"  have  the  same
     effect,  they  create  an object file from the source in [12,10].
     The command ASSEMBLE given without any parameters would result in
     the  prompt  "Filename?"  since the specification for the command
     requires at least one parameter, and it is to prompt for one par-
     ameter if it is not present.  The specification ensures that "M "
     is matched by the single character alone,  and  ASSEMBLE  by  the
     characters AS ASS ASSE ASSEM thru ASSEMBLE.


                            KEYWORD LINES
     $mnpqKEYWORD	
     		First line of a command set.  There may be many
     		keyword lines for the same action line.
      
     	m	Minimum number of characters to match.
     	n	Maximum number of characters to match (extra ignored).
     		(ignored in current version but must be present).
     	p	Minimum number of parameters required.
     		If this number of parameters is not present then
     		parameters will be prompted for.
     	q	Maximum number of parameters to question for.
     		In the case where prompting occurs then this number



                                                                PAGE 6



     		is the highest prompt to be requested.
      
     		The keyword may consist of up to 8 characters to be 
     		matched identically by the CCL processor. The only 
     		terminators for the keyword typed by the user are <space> 
     		and <carriage return>.
      
      
      
     ?nQUESTION
     		Where n is the parameter number (they should be in order)
     		in the range 1-9 . If the correct number of parameters are
     		supplied no questions are asked, otherwise questions are
     		asked and the associated parameters are filled in.
     		If parameters are skipped then they will only have values
     		if they were given on the original command line.
      
      
     *COMMAND LINE parasub1 parasub2 parasub3 ......
      
     		Command or Action lines are indicated by a '*' in 
     		column 1.  Their text is copied except that parameters 
     		are substituted.
      
     	parasub
      
     		%n { absent } { absent } %
     		   {   ,    } { .ext   }
     		   {   =    } { ;gen   }
      

          The '%'  denote  a  parameter  substitution  argument.   The
     number  n is the number of the associated parameter to be substi-
     tuted.  Each parameter must be seperated by a  delimiter.   Valid
     delimiters  are:   space,  comma(','), '=','<', '<-'.  A [UIC] is
     treated as a special case in that the comma seperating the  group
     and  member numbers is not treated as a delimiter(all of the UIC)
     can be one parameter.

          The first group of optional elements denote a  character  to
     be  inserted  before  the parameter if the parameter is not null.
     Only ',' or '=' may appear in this  position(ie  be  inserted  in
     front  of the parameter).  The second group denote elements to be
     appended if their initial character is not present in  the  input
     parameter  string.   Typically  these are only those which denote
     file extensions and version numbers.  Finally a '$' is interpret-
     ed  as  as  an 'escape' key to be used in terminating the command
     rather than MCR.

     From the above examples:

     In ASSEMBLE / M the filename given would normally be a plain name
     eg MCRDIS which would result in 
      
     	MAC MCRDIS=[1,1]EXEMC/ML,[11,10]RSXMC/PA:1,[12,10]MCRDIS
      
     In LIST or TYPE since the required number of arguments is set  to
     one,  and  the  number of arguments to be prompted for is one the
     results are
      



                                                                PAGE 7



     TY file		-> PIP TI:=file.MAC
     T file.slp		-> PIP TI:=file.slp
     TYPE file,file2	-> PIP TI:=file.MAC,file2.MAC
     TYPE
     FILE?myfile	-> PIP TI:=myfile.MAC
      
     COMPARE MCRDIS
     Output? TI:	-> CMP TI:.SLP/SL=MCRDIS;-1,MCRDIS
     CO
     Files? INDROT
     Output? INDROT	-> CMP INDROT.SLP/SL=INDROT;-1,INDROT
      
     or alternatively with the definition
      
     	$2722COMPARE
     	?1Files
     	?2Output
     	*CMP %2%%1.SLP%/SL=%1;-1%,%;0%
      
     one then has
     MCR>COM
     Files? INDROT
     Output? 		-> CMP INDROT.SLP/SL=INDROT;-1,INDROT;0
     or
     MCR>COM
     Files?INDROT
     Output?TI:		-> CMP TI:INDROT.SLP/SL=INDROT;-1,INDROT;0
      
      however altering this to
      
     	$2712COMPARE
     	..........
      leads to
     MCR> COM INDROT	-> CMP INDROT.SLP/SL=INDROT;-1,INDROT;0
     MCR> COM INDROT TI:-> CMP TI:INDROT.SLP/SL=INDROT;-1,INDROT;0
     and
     MCR> COMPARE
     Files?INDROT
     Output?TI:		->       ditto
      
     Because the number of parameters to prompt for was set to 2 
     if the required of 1 was not present.
      
     EXAMPLE:
      
     1.  UIC		==>  SET /UIC
     2.  UIC  [G,M]	==>  SET /UIC=[G,M]
     3.  UIC =[G,M]	==>  SET /UIC=[G,M]
      
          The following entries in SYSCCL.CCL produce the above
      syntax.
      
     		$3300UIC
     		*SET /UIC %2=%%1=%
      
       Case 1.	No parameters present so   SET /UIC sent out.
      
       Case 2.	Since only one parameter is present ([G,M} {Remember
     		the comma in a UIC is not a delimiter.}, %2=% evaluates
     		to a null and %1=% evaluates to  =[G,M].



                                                                PAGE 8



      
       Case 3.	The = sign (UIC =[G,M]) acts as the first delimiter
     		which means parameter 1 is evaluated to a null and
     		parameter 2 is evaluated to be =[G,M].
      
      
     EXAMPLE:
      
     DIRECTORY filespec		==>PIP filespec/BR
      
          The CCL entries to produce this command would be
      
     		$3900DIRECTORY
     		*PIP %1;*%/BR
      
       Case 1.	The command DIRECTORY would have parameter 1 as 
     		null so the MCR command would be  PIP /BR.
      
       Case 2.	The command DIR *.CMD would have appended a ;* 
     		since there is no ';' in the command line typed in.  
     		So the command is passed back to MCR would be  
     		PIP *.cmd;*/BR.
      
       Case 3.	The command DIR *.CMD;1  would have nothing appended 
     		since a ';' is found in the input commnad.  Hence, 
     		the command PIP *.CMD;1/BR  would be sent to MCR
     		by CCL.



                                                                PAGE 9



                              APPENDIX B


               PASSING COMMAND LINES VIA THE RUN COMMAND


     Running a task via the RUN filespec facility causes the system to
     RUN  the  task and remove it on exit.  In reality MCR decodes the
     RUN command and then  issues  an  INS  filespec/RUN=REM/TASK=TTn.
     The /RUN=REM switch specifies that the task is to be removed from
     the installed task list when it exits.  In a standard RSX11M sys-
     tem  there  is no way to pass the task an MCR command line unless
     it is installed as an external MCR command(...XYZ).

          To partially bypass this restriction, a new switch has  been
     added   to   INS(and   hence   the   RUN   command),   the   /PRM
     switch(parameter).  The syntax is
      
     		RUN filespec/PRM=txt
     or
     		RUN filespec/PRM="txt"
      
     where 'txt' is an ASCII command string.  Both forms of  the  /PRM
     switch  do  the same thing.  However, if the command to be passed
     to the task when it is running is to include a switch(ie  a  '/')
     then the form using the "txt" is required.

          It should be pointed out that a normal MCR command line  may
     be  up  to 80 characters long.  The longest command line possible
     via the RUN command is 57 characters(if filespec is 9  characters
     long).  Adding a /TASK=TSKANM switch , or a /PRI=N switch further
     decreases the maximum length in a command by 12 and 7  characters
     respectively.   CCL  checks to see if an expanded command line is
     <80  characters  long.   If  not  it  issues  an  error  message.
     However, when used CCL is used with the RUN command, error check-
     ing is more difficult because of  the  implicit  /RUN=REM  switch
     which  is  automatically inserted into the command line by SYS as
     the command is passed on to INS to Install, Run, and  Remove  the
     task.   If  it is desired to have CCL do as much checking on com-
     mand line length as possible, prototype command lines  in  either
     USERCCL.CCL  or SYSCCL.CCL should avoid using the RUN command and
     should replace it with INS filspec/RUN=REM.


     EXAMPLE:
      
     	RUN LB:[1,53]DMP/TASK=...DMP/PRM="TI:=3831.ARC/AS"
        or
     	INS LB:[1,53]DMP/TASK=...DMP/RUN=REM/PRM="TI:=3831.ARC/AS"
      

          If command lines are not expected to be long and the task is
     frequently  used  by a large number of users, the CCL command can
     RUN (INS /RUN=REM) the task with a taskname of the  form  ...XYZ.
     This  means  when  the next user goes to use the task, and if the
     first user is still using the task, multiple copies of  the  task
     will  be  created, one for each terminal using the task.  As each
     task exits it will be removed from the installed task list.  This
     cuts  down  somewhat  on  the overhead of looking through the CCL
     command files.  A simple example of this is BASIC on our  system.



                                                               PAGE 10



     BASIC  is not normally an instaled task, rather when a user types
     BASIC, CCL runs BASIC and installes  it  with  the  name  ...BAS.
     Once  the origional copy of ...BAS is active, multiple copies can
     be created at various terminals.  For tasks  which  require  long
     command  lines(BASIC  requires none), this method is not suitable
     and it may be necessary  to  RUN  the  task  without  the  /TASK=
     switch.   This  means  that the task will be run with the name of
     the terminal(TTN).  



                                                               PAGE 11



                              APPENDIX C


             PASSING VARIABLES TO INDIRECT COMMAND FILES


     The Indirect File processor(.AT)  has  been  enhanced  to  accept
     passing parameters on command lines.  One may now type
      
     		@CMDFILE ,PARAM1, PARAM1, PARAM1, PARAM4,.....
      
     and have the parameters PARAM1.....PARAMn transfered to variables
     in  the  indirect  file  processor.(PARAM1  ->  $A, PARAM2 -> $B,
     PARAM3 -> $C.

          AT.  now defaults to .ENABLE GLOBAL as it starts up, and the
     parameters  are passed to the GLOBAL variables $A,$B, ....  which
     are automatically defined as they are needed.
      
     EXAMPLE:
      
          A powerful example of using this is the BUILD CCL command.
      
     	BUILD tsknam,(NO)LIST,(NO)BUILD,(NO)MAP,(NO)YES
      
     This command passes the string variables 
      
     		tsknam,(NO)LIST,(NO)BUILD,(NO)MAP,(NO,YES)
      
     to @[1,5]BATCH/NOLI,PARM1,PARM2,PARM3,PARM4.  Here tsknam is  the
     name  of  the  FORTRAN  IV  file  to  compile,  with or without a
     listing(LIST, NOLIST),BUILD or NOBUILD, determine whether or  not
     to  taskbuild(with  or without producing a MAP), and able(YES) or
     not albe(NO) to be run by other users.  A listing of BATCH.CMD is
     provided as a guide to writing complicated command files to which
     CCL passes parameter strings.  Note in the listing  that  .IFNEXI
     is  used  to test to see whether or not the source file requested
     exists, and the command file @BATCH creates, tests to see if  the
     F4P  compilation  produced an object module.  If no object module
     is produced, the command file terminates gracefully, saving  sub-
     stantial time.



                                                               PAGE 12



                              APPENDIX D


                 MODIFICATIONS TO CCL FOR V3.2 RSX11M 



          CCL is slightly modified(it certainly could  use  some  more
     work) for the V3.2 release.  Exit with status has been added.  If
     a CCL command can not be executed (file not found, line too long,
     etc)  a  fatal  exit status of 4 is returned to the indirect file
     processor.  Eventually, it is hoped to be able to get exit status
     from the spawned task.  As of BL25 (field test) this was not pos-
     sible due to a bug in mcr in passing on exit  status  information
     from  tasks  which  had been run.  It is expected that it will be
     possible in the final V3.2 release to return exit status  on  all
     ccl commands to the indirect file processor task.

          CCL now can be built with the SPAWN directive if it is  ava-
     ilable.   CCL  requires the EXST$ (Exit With Status) directive in
     order to return exit status..  Modules exist to  build  CCL  with
     the  SPAWN  directive, the PUTMCR directive or the MCR driver.  A
     check is now made to see if the expanded command line is  too  is
     too  large  to fit in an MCR buffer.  This saves much frustration
     when one enteres l
ongish commands, and the tasks reject  them  at
     some  unknown point in the command line.  If CCL detects that the
     command is too long to pass on , it warns the user and prints out
     the offending line up to the point at which it overflowed the al-
     lowed line length.

          Since the various PIP, CCL commands seem to be the most used
     and   useful,   these   commands(BRI[EF],   DIR[ECTORY],  LIS[T],
     DEL[ETE], PUR[GE], SPO[OL], AND TRU[NCATE]) have been  explicitly
     built  into  CCL's  command parsing.  This speeds up command res-
     ponse quite noticeably on system with slow disks.