SYSLOG, TSKLOG, LOGTSK,  and ACC
   SYSTEM RESOURCE ACCOUNTING AND PERFORMANCE MEASUREMENT FOR RSX11M V3.2


     Past History of Accounting for RSX11M

          Since Multi-User protection was  implemented  on  RSX11M,  the
     user community has felt a need for tools with which to measure sys-
     tem performance and to account for  the  system's  usage.   Various
     users  have  implemented  accounting schemes of one form or another
     over the past few years to satisfy  their  local  needs.   Some  of
     these  methods  have  been  found to be generally applicable to the
     community at large.  The accounting package developed at McGill Un-
     iversity  is  now marketed by GEJAC, INC.  It is aimed primarily at
     charge back accounting to the user's.  A system for terminal  usage
     accounting  and run privlege allocation was developed by KMS Fusion
     and has been used by many systems not needing  accounting  for  CPU
     time usage.  A limited task accounting scheme was developed by Greg
     Basset(DEC).  It was aimed at measuring the performance  parameters
     (CPU time, QIO count) for a list of tasks input from the console.

          RSX11M-PLUS has an accounting system which provides hooks  for
     measuring  performance  of  the  system,  and  also provides enough
     statistics for providing chargeback accounting if it is so desired.
     The  M-PLUS  accounting scheme is not suitable for use on an RSX11M
     system.  Firstly, if it is selected as a  SYSGEN  option,  a  small
     system  overhead  is  imposed.   Secondly,  its design was based on
     eventually having to implement task accounting.  This has made  the
     scheme  substantially  more complicated than one which was aimed at
     providing performance measurement tools for tuning  the  system  as
     its  primary  goal.  Thirdly, it uses up a lot of pool.  Pool space
     (and core space) is much more limited on a standard  RSX11M  system
     than on an M-PLUS system running on an 11/70.  Fourthly, it creates
     rather large log files.

          This package is the result of an attempt to  incorporate  most
     of  these features as well as provide statistics suitable for moni-
     toring system performance in a manner consistent with  the  limita-
     tions of an RSX11M system.


     System Overview

          Version 3.2 of the KMS FUSION accounting system  is  aimed  at
     providing the user of RSX11M V3.2 with a versatile tool for measur-
     ing the performance of the operating system, tuning the system, and
     providing  sufficient  usage  statistics so that the system manager
     can implement chargeback accounting if it is required by  the  ins-
     tallation.  Sufficient hooks are provided so that the intrepid user
     can expand the system substantially beyond what is  currently  pro-
     vided.

          The basic system  is  implemented,  incorporating  only  minor



                                                                  PAGE 2



     changes  in  the EXEC data base(SYSCM) and TDSCH.  The user is able
     to select on an individual basis, CPU time accounting, global  per-
     formance  parameter  logging(shuffler  requests,  loader  requests,
     checkpoint requests, system null time tics), total system QIO's is-
     sued,  user  by  user  QIO totals, logon/logoff statistics for each
     terminal, memory usage and pool usage logging, CO:  statistics log-
     ging,  and disk block usage at logoff.  Additionally, task account-
     ing for selected tasks is provided.  A summary of  the  data  which
     may be gathered and logged is seen in the following table.


     GLOBAL:	Exec Null Time		USER:	Logon/Logoff Times.
     		# Run requests			Account # and Terminal ID
     		#LDR Requests			CPU Time.
     		# checkpoint Requests		# QIO's Issued(optional).
     		# SHF Requests			# Illegal Login Attempts.
     		# QIO's Issued(optional)	Disk Usage(# files 
     						    and disk blocks).
     						# RUN requests.
     						# ...AT. runs.
     						# INS runs.
     						# Pages Printed(optional).
     CO:	# QIO's Issued(optional)
     		CPU Time.
     		# RUN requests.
     		# ...AT. runs.
     		# INS runs.
      
     MEMORY:	# Tasks in Core	 	TASK:	Stop Time.
     		Total Memory in Use		Run Time.
     		# Tasks out of core.		CPU Time
     		Total Memory Checkpointed	# QIO's Issued.
     		Total free Pool.
     		Largest fragment in Pool
     		# fragments in pool.

          The system is composed of four tasks;   1)  an  MCR  interface
     task  ACC which will control and reconfigure accounting on-line and
     display the current status of accounting, 2) the  accounting  task,
     SYSLOG,  which will insert hooks into the EXEC to implement the ac-
     counting code, 3) a logging task which will  recieve  data  packets
     from  SYSLOG,  HELLO,  BYE, TSKLOG, and UPD, and 4) the task TSKLOG
     which implements task accounting for a list of tasks input  at  the
     user's  terminal.   The  task accounting is designed primarily as a
     performance measurement tool.

          Accounting information accumulates in  two  places.   Terminal
     connect time, user CPU time, and user disk blocks in use is updated
     in the system account file RSX11.SYS at each logoff(for both  TT:'s
     and  VT:'s).   For instance if only CPU time accounting is enabled,
     the system logging file(SYSLOG.DAT) will only  accumulate  data  on
     when system logging starts and stops.  This is compatible with sys-
     tems which are severely limited in disk storage space and only  oc-



                                                                  PAGE 3



     casionally want to activate additional accounting features.  In ad-
     dition the user may select that system wide and user statistics  be
     logged  to a file(LB:[1,4]SYSLOG.DAT).  The data in the log file is
     readable via a standard F4P task.  The format of the  data  packets
     sent  to LOGTSK is to be found in TABLE II at the end of this docu-
     ment.  Sufficient data is logged to provide terminal usage  profil-
     ing,  total  system  utilization, user disk block usage at each lo-
     goff, CPU time used by each account, system total QIO's issued  and
     a  user by user total of QIO's issued.  In addition, a user by user
     count is kept of the number of tasks run(activated) by a user,  the
     number of uses of INS, and the number of times ...AT is run.

          The task SYSLOG will log the global  system  statistics  every
     'DELTA' minutes, issue a mark time, and stop itself until the mark-
     time is satisfied.  By varying the sampling time the user  may  get
     as  fine  or  as coarse a picture of the system as is desired.  The
     parameters which are sampled, logged and reset are chosen  to  pro-
     vide  insight  into  how the system is performing, ie QIO's issued,
     SHUFFLER requests, LDR requests, checkpoint requests,  and  current
     memory  usage  statistics(pool, number of tasks in and out of core,
     and size of tasks in and out of core).

          At present certain enhancements to the package are being  con-
     sidered  for the second release.  Eventually it is hoped that minor
     modifications can be made to LDR and SHF so that a distinction  can
     be  made  between  the  number  of  LDR or shuffle requests and the
     number of times these tasks run.  This would  provide  much  needed
     information on how much trashing the Exec is doing.  In addition to
     system wide and user by user QIO accounting, it would be  also  ex-
     tremely  useful in determining bottlenecks, if information could be
     accumulated on the number of QIO'S for each device(not just  termi-
     nals).   Finally, TSKLOG should be made optionally to work off of a
     list of tasks stored in a file rather than from terminal input.


     Design Constraints/Goals

          Since RSX11M is primarily used by many users for its fast real
     time  response  and functionality on a small PDP11 system, a number
     of constraints are imposed in the beginning on  any  implementation
     of a suitable accounting/performance-measurement system.
      
     1.  There must be no system overhead if accounting is disabled.
     2.  Accounting must be reconfigurable on line.
     3.  Sufficient hooks must be present so that the user can monitor
         system performance, locate bottlenecks, etc.
     4.  It should be easly extensible by a user.
     5.  Sufficient information should be provided such that a user
         can implement any type of charge back accounting desired.
     6.  The accounting system's overhead must be an absolute minimum.
     7.  Accounting must not drastically decrease the system's pool.
     8.  Accounting must not use undue amounts of disk space.
     9.  The methods used to implement accounting must not use an 



                                                                  PAGE 4



         additional APR because it is desirable that HELLO be 
         buildable with an FCS resident library.

          These goals are met by this implementation of the KMS Account-
     ing  System.  It should be emphasized that previous features of the
     KMS Fusion Accounting/Enhancement package for RSX11M are either re-
     tained  or  their  functionality  is enhanced.  System resourse ac-
     counting may be addded to these features to provide a  system  per-
     formance  measurement  tool  or charge back accounting on a user by
     user basis.

          In order to be able to maintain the ability of HELLO to  build
     with an FCS resident library and a 16K exec, it was decided to mod-
     ify the Executive and terminal data bases rather than installing  a
     common  partition  for accounting.  As it turned out, the data base
     changes were by far the easiest part of the task.

          It also would have been possible to have  an  accounting  task
     which  kept  all  its  data internal to its node pool.  This method
     avoids having to do a SYSGEN but has several  severe  disadvantages
     from our standpoint.  Firstly, if the task is ever aborted by acci-
     dent, one must reboot to start up accounting.  Secondly,  no  other
     tasks  can know anyting about the location of the accounting termi-
     nal accounting nodes.  This makes it much more  difficult  to  have
     tasks  like MCR...  bump counters each time ...AT is run.  All such
     counting must be done by sending messages  to  the  system  logging
     task.   On  an  active system this can pose substantial overhead as
     well as filling pool with send  packets  if  the  logging  task  is
     checkpointed  out  for  a  while.  Also, it is far faster to bump a
     counter at a known location than it is to scan  for  an  accounting
     block.   Finally,  by  using  storage  in  a  terminal's  own  UCB,
     privleged tasks have fast access to both their  current  QIO  count
     and  CPU  time.   This  makes  it relatively easy to implement time
     critical performance measurement tools to monitor a task's through-
     put and disk access time.


     System Requirements

          For this release no attempt has been made to make this package
     universally  usable  by all users.  It should however, be usable by
     most users with no changes and  by  nearly  all  users  with  minor
     changes.   It  is  assumed the prospective user has a mapped system
     and has selected multiuser protection and support for all executive
     directives.  Not all executive directives are used by this package,
     but such a system is closest to the one the package  was  developed
     on.   (In the past, I have discovered that If one wants to SYSGEN a
     system which will require the fewest DEC patches over its lifetime,
     it  is best to select a system with all the options because this is
     the system which has likely gotten the most testing  by  DEC.)  The
     prospective  user  will  have  to  do  a  SYSGEN to incorporate the
     changes in the data bases for CO:, TT:, VT:  and SYSCM.  The modif-
     ication to TDSCH.MAC must be done to define the variable UPTIM as a



                                                                  PAGE 5



     global symbol.  For this SYSGEN only those changes  need  be  done.
     All  other  components  can be brought up piecemeal as time allows.
     However, the data structures required must be created via a  SYSGEN
     even  if they will not be immediately used.  Three SLP files modify
     the SYSGEN command files to correctly ask questions concerning  the
     options  desired,  and to generate the correct data bases.  Two SLP
     files modify the EXEC modules SYSCM and TDSCH.  Making these modif-
     ications  will in no way result in a corrupted system or cause fla-
     key crashes.  

          In addition to changing  UPTIM  to  be  a  global  symbol  the
     TDSCH.SLP file implements a change which allows modifying the ROUND
     ROBIN schedule interval and disk swapping interval on  line.   (The
     task SCH does this).  Modifications to SYSCM provide the system ac-
     counting tasks with common storage  variables  and  defines  a  new
     quantity  LIBUIC.   This  later change was put in because ...AT can
     use it if it exists(an M-PLUS feature).  Modifications to  the  set
     parser  allow LIBUIC to be displayed and changed.  Modifications to
     INS allow the RUN $FILENAME to search first to SYSUIC and  then  on
     LIBUIC.   Hence  it is easy to have seperate directories for privi-
     leged tasks and the common utilities.

          While  a  number  of  standard  privleged  EXEC  modules   and
     privleged tasks get minor changes, all tasks can test an accounting
     feature mask, $ACMSK, to see if they are to execute accounting code
     or not.  With as little as the addition of $ACMSK to SYSCM a single
     object module for a privleged task could be  used  for  creating  a
     task  image  for  any system.  Reassembly would not be necessary if
     all options were initially selected.  It is assumed that  the  user
     desiring to implement this enhancement has sufficient skill to do a
     non-standard SYSGEN, apply SLP files and decide on what trade  offs
     his/her  system  can  tolerate  to support acounting.  A bare bones
     system with only 2 RK05 disks, minimal free pool, only 32 kwords of
     memory,  and  lofty  goals  will  have difficulty implementing, and
     using this package.  Other users should have very little  difficul-
     ty.  

          It is assumed that the user has  selected  multi-user  protec-
     tion,  and  the stop bit directives.  The code in TSKLOG for an un-
     mapped  system  has  never  been  tried   by   me,   and   is   not
     guaranteed(supported??).  

          It goes almost without saying that nothing is without a  cost.
     While  the  accounting  system  is very efficient and imposes a low
     overhead on the operating system(real time compatable), it does use
     up a certain amount of pool space.  If CPU time accounting, QIO ac-
     counting, and run privlege allocation are all desired, about 80(10)
     words  of pool are used up by a node of PIC code.  If task account-
     ing is selected the size of SYSLOG's code node  increases  slightly
     and of course there is TSKLOG's code node also to consider.  An ad-
     ditional 7-9 words are used for each terminal UCB.  SYSCM  requires
     12-25 extra words in its data base depending on the options select-
     ed.  The SLP file provided creates a few more words  than  this  in



                                                                  PAGE 6



     SYSCM  for future expansion.  The variables $LDRCT, $SHFCT, $RUNCT,
     and $CKPCT all may be commented out.  They  are  there  to  provide
     hooks for the next release which will try to provide information on
     executive thrashing(compare various request counts with actual exe-
     cution  of  the  request).   The symbol $SPARE(4 words) may also be
     commented out.  I use it for testing out concepts  requiring  extra
     symbols  in the Exec, before actually commiting to a SYSGEN.  Table
     I provides a summary of the various size chages, and pool usage re-
     quirements imposed by the various options.

          As mentioned before, to incorporate this package a SYSGEN must
     be performed.  While the overhead of this package is low, it is not
     zero.  The most significant overhead occurs at each clock tic.   If
     the system is executing a task, each clock tic, 11 instructions are
     added to the clock ISR code.  If the EXEC is in its idle loop 5 in-
     structions  are  added  to  the  clock  ISR.  This presents a small
     overhead for systems with a 60 Hz line clock or a 100  Hz  program-
     able  clock.  Using this package with a faster programable clock is
     not recommended.  For 60-100Hz clocks perhaps as much  as  5%  more
     code must be executed each clock tic(see TDSCH.MAC).  This account-
     ing system(or any system for that matter) probably is not well  su-
     ited  for  an  operating system with tasks doing very time critical
     interrupt processing.


     				TABLE I
      
     		 MEMORY REQUIREMENTS FOR KMS SYSTEM ACCOUNTING
      
      
      
     	     				         SYSLOG	     TSKLOG
     			   SYSCM     TT: UCB	CODE NODE  CODE NODE
     			----------------------------------------------
     	KMS RUN PRIV	!     2    !     1     !          !          !
     			----------------------------------------------
     	CPU TIME	!          !     3     !    24    !          !
     			----------------------------------------------
     	GLOBAL ACC.	!    10    !     3     !    30    !          !
     			----------------------------------------------
     	USER QIO ACC.   !          !     2     !    24    !          !
     			----------------------------------------------
     	MEMORY ACC.	!      	   !           !          !          !
     			----------------------------------------------
     	TASK ACC.	!     6    !           !    26    !   284    !
     			==============================================
     	TOTAL WORDS	!    18	   !     9     !   124    !   284    !
     			!          ! PER UCB   !ALL OPT.  !+10/TASK  !
     			==============================================
      

          This table's function is to give a rough idea as to what vari-
     ous options cost in terms of lost pool.  Note that the conditional-



                                                                  PAGE 7



     ization of options is not yet complete and some  options  automati-
     cally  drag in others.  This is the case with the TT:  UCB changes.
     The data block for user global accounting is  lumped  in  with  CPU
     time accounting.  If the user is very careful to change all offsets
     to U.QIO1 and U.QIO2 in all of the supplied programs and slp files,
     the  section  of  each  terminal's UCB reserved for global user ac-
     counting may be removed(3 words).





                                                                  PAGE 8



     System Components

          The accounting system is composed of a number of non-DEC tasks
     and   SLP  files  for  modifying  certain  RSX11M  source  modules.
     Incorporating the system will involve a  system  generation  (which
     has become a rather simple matter for V3.2.).
      
     ACC.MAC		The account task dispatcher/controler.
     ACTFIL.MAC		New account file offset definitions.
     LOGTSK.MAC		The log task.
     SYSLOG.MAC		The central accounting task.
     TSKLOG.MAC		The task accounting task.
     ACNT.SLP		Enable an existing option to ACNT.
     BYE.SLP		Modification to DEC bye.
     HELLO.SLP		Modification to DEC hello.
     INSHD.SLP		Counts usage of INS (please apply all INS 
     			SLP files, not just INSHD.SLP).
     JOBEND.OBJ		Enables logging of print spooler usage.
     MCRDIS.SLP		Counts usage of ...AT., enables usage of PIN
     			and fixes several MCR bugs.
     SYSGEN.SLP		If you want all loadable drivers and all loadable
     			user written drivers, you don't have to edit
     			RSXBLD.CMD.
     SGNEXEC.SLP	Create new assembly parameters in each RSXMC.MAC.
     SGNPER.SLP		Modify CO:'s data base.
     SGNTT.SLP		Modify data base for terminal's.
      
     In addition, modifications to the standard KMS  Fusion  enhancement
     package have been supplied which are compatable with the system re-
     source accounting.  Included in this catagory are updated  versions
     of  modifcations to RESET(zero CPU time when clock time zeroed), to
     ACCLOG(display the used CPU time and  %  system  utilization),  WHO
     (show  who is using BATCH), and BATCH(log VT:  CPU time and use PIN
     instead of ...AT.).


     Component Description


     ACC -- User Interface Task

          The task ACC is used to start accounting, stop accounting, en-
     able  and  disable  accounting  features on line, and display those
     features currently active.  It has the following functions.
      
      
     1.	Start accounting.
     2.	Set the account feature mask for the desired options.
     3.	Change the accounting features desired(except for cpu
     	time, null time and QIO accounting) on line without
     	interupting accounting.
     4.	Modify the accounting sample interval.
     5.	Turn off accounting.



                                                                  PAGE 9



     6.	Display the current accounting features.
     7.      Start/Stop task accounting.
      
     command syntax:
     			ACC /sw1/sw2/sw3 ...
      
     where the switches are
     	
     START	- Start up the accounting task SYSLOG.
     STOP	- Stop the accounting task SYSLOG 
     CPU 	- Start CPU and null time accounting .
     GBL	- Log system global variables at each interval.
     QIO	- Activate system wide qio accounting.
     UQIO	- Activate system wide and user qio accounting.
     DIR	- Activate directive accounting.
     MEM	- Log memory utilization variables every sample interval.
     FREE	- Log memory utilization variables if core space is tight
     		  or if the checkpoint files are in significant use.
     POOL	- Log memory utilization variables if pool gets too low.
     DLT:N	- Change sample interval time, to n minutes .
     		  Defaults to 30 minutes.
     LOG	- Log HELLO/BYE/UPD sign on/off times, statistics,
     		  and terminals.
     DSP	- Display current settings of account mask.
     LCO	- Log co: statistics each sample interval.
     TASK	- Start up task accounting, requires /UQIO
     PRI[NT]	- Print task accounting statistics to TI: (not log file.)
     SPO[OL]	- Enables logging of print spooler usage(new spooler).
     NUQ[IO]	- Disable terminal qio accounting.
     		  (system wide qio accounting continues).
     NLO[G]	- Disable logging hello/bye/upd data.
     NLC[O]	- Disable logging co: statistics.
     NME[M]	- Disable memory logging.
     NFR[EE]	- Disable memory logging on low free core.
     NPO[OL]	- Disable memory loggig on low free pool.
     NTA[SK]	- Disable task accountin.
     NPR[INT]	- Disable printing task accounting to TI:
     NSP[OOL]	- Disables logging print spooler usage.
      
      
     * -- All options enable CPU time accounting.


     Switch Description


          /START

               The /START switch must be used on the command line start-
          ing up accounting.  It must be followed with other switches in
          order to define the type of accounting configuration  desired.
          ap  When  accounting  starts up, a start packet of data (start
          time, sample interval, and $ACMSK) is sent to LOG...



                                                                 PAGE 10



          /STOP

               The /STOP switch will stop system accounting and task ac-
          counting(if  active).  It should be issued as a command by it-
          self.   Before  SYSLOG  exits  a  stop   data   packet   (stop
          time,schedule  interval,  requesting task, and $ACMSK) is sent
          to log...


          /DSP

               The /DSP switch will display  all  currently  active  ac-
          counting  options including the sample interval.  It should be
          used on a command line by itself as it will display  the  cur-
          rent status as soon as it is decoded.


          /CPU

               The /CPU switch indicates  that  CPU  accounting(the  de-
          fault)  is desired.  The /CPU switch need not be used if other
          accounting configuration switches


          /GBL

               If the /GBL switch is  present,  every  'DELTA'  minutes,
          various  global accounting parameters are scanned and account-
          ing data packets sent to log.  At present  the  global  system
          statistics include run requests, SHUFFLER requests, checkpoint
          requests, and LDR requests.  Until  core  becomes  very  over-
          crowded, these statistics provide a good measure of system ac-
          tivity in any period of time.  If too many tasks are competing
          for  core,  the  Exec  will thrash about swapping tasks in and
          out.  SHF will start being requested very  often  even  though
          there  is nothing it can do.  If this accounting shows this to
          be a persistant and serious problem the task SCH  is  provided
          which  can  modify the Round Robin and Executive Disk Swapping
          intervals on line.  By lengthening these times, tasks will  be
          allowed  to  execute longer and thrashing should decrease to a
          manageable level.  

               Run requests(tasks started via RUN, MCR commands,  spawn-
          ing  or  requesting will be counted globally in SYSCM and also
          counted in each owning terminal(of CO:)  UCB.   Tasks  already
          active  will  not be counted(ie stopped tasks) if they are re-
          quested(like MCR...).  If user accounting is selected BYE will
          send  off  the user run count to LOGTSK with it's send packet.
          In addition BYE will display a summary of the  user's  connect
          time,CPU time, and number of tasks run(just like RSX11M-PLUS).


          /QIO, /UQIO, and /NUQIO



                                                                 PAGE 11



               If  /QIO  accounting  has  been  selected  as  a   SYSGEN
          option(it  must  for task accounting to work), the /QIO switch
          will enable SYSLOG to keep a count of the total  system  QIO's
          issued.   This  value  is  sampled every 'DELTA' minutes.  The
          counter is a 2 word counter, but for a system with  a  lot  of
          QIO  activity  some  care  must be excersized in selecting the
          value for 'DELTA' to insure that overflow does  not  wipe  out
          the data.

               The /UQIO switch enables user by user qio accounting.   A
          count  of  the  number  of QIO's issued at a given terminal is
          made into each UCB.  This counter is zeroed at logon,  and  at
          logoff  its value is sent to LOGTSK.  The switch /NUQIO may be
          used to turn off user by user QIO accounting  unless  tasklog-
          ging  is operative in which case, using the switch is declared
          to be an error.  System wide QIO accounting may not be direct-
          ly  disabled while SYSLOG is running.  To turn off system wide
          QIO accounting, issue a ACC /STOP and when SYSLOG stops, issue
          another command to start it up with the appropriate option.


          /MEM, /NMEM

               The   /MEM   switch   enables   accounting   for   memory
          utilization(if it is a sysgen option).  A section of code bor-
          rowed from RMDEMO of the number of tasks in core,  the  number
          of tasks out of core, the size of task in core and the size of
          tasks out of core(checkpoint files).  Additionally,  it  keeps
          track  of  pool(free  pool,  largest size, and number of frag-
          ments).  The /NMEM switch disables logging memory statistics.


          /FREE, /POOL, /NFREE, and /NPOOL

               Memory utilization accounting can use up a  lot  of  disk
          space  quickly.   Often  all  one wants is to keep a record of
          when the system started to hang up(too little pool, too little
          memory,  too  many  tasks  in  and  our  of core, or too large
          tasks).  The /FREE switch directs SYSLOG to send off a  memory
          utilization  data  packet  only if core space gets tight or if
          too many files are on checkpoint files.  Currently Syslog will
          send  off a memory record if /FREE is implemented if more than
          75.K words of tasks are in core or if more than 10.K words  of
          tasks  are out of core.  These values should be changed to re-
          felect the size of free core on one's system and the total am-
          ount  of checkpoint file space available.  Edit SYSLOG.MAC and
          Pf Inval.  The switch /NFREE will disable this accounting fea-
          ture.   The  POOL  switch will do the same thing for pool.  If
          the /POOL command switch is present, a memory  utilizaton  re-
          cord  will be logged every sampling interval during which pool
          is less than 500(10) words.  However if pool is 200(10)  words
          or  lower,  no  data will be sent, rather a counter(NOPOOL) is
          incremented to show how many times low pool would have  forced



                                                                 PAGE 12



          logging  pool  and memory statistics.  The value for NOPOOL is
          sent with each send packet and is then cleared.   /NPOOL  dis-
          ables this option.


          DLT:n

               The /DLT:n switch set the sample interval to be  'n'  mi-
          nutes.   At  startup  if no sample time is specified, a sample
          time of 30 minutes is assumed.  Any time thereafter  the  /DLT
          switch may be used to change the sampling interval.  Each time
          the sample interval is changed a change sample  interval  data
          packet  is  logged.  This enables a program reading SYSLOG.DAT
          to keep track of what is happening.  LOGTSK  is  sensitive  to
          the sampling interval.  If the samples are more than 5 minutes
          apart, it exits between times when it recieves data.  If  sam-
          ple intervals are more frequent, it stops itself and waits ar-
          ound for data to show up.  This eliminates the overhead  asso-
          ciated with opening/closing the log file.


          /LOG, /NLOG

               If the /LOG switch is specified, HELLO, BYE, and UPD  all
          send  off  data  packets  to  LOGTSK.  The /NLOG disables this
          function.  HELLO sends to LOGTSK the logon time, the  terminal
          ID,  the  account  number,  the  UIC and the number of illegal
          login attempts since the last logon.  BYE sends off the logoff
          time,  the terminal id, the acnt number, the UIC, the CPU time
          used, and the number of QIO's issued by the user.   UPD  sends
          off  the logoff time, the terminal id, the account number, the
          user's system device, the number of  files  in  use,  and  the
          number  of  blocks  in use.  From the data sent by these three
          tasks a sophisticated chargeback system could be implemented.


          /LCO, /NLCO

               A large number of tasks run with CO:  as their TI:.  Some
          of  these are system tasks while others are real time tasks or
          tasks which have been scheduled.  In order to  keep  track  of
          the  system  resources used by these tasks, the /LCO switch is
          provided.  The SYSLOG intercept code will log  data  to  CO:'s
          UCB  just as if it were a real terminal(this is why we require
          the  CO:   driver  data  base).   Every  'DELTA'  minutes  the
          data(CPU time and QIO count) is logged and the values reset to
          zero.  The /NLCO switch disables logging of data from CO:.


          /TASK, /NTASK

               If TSKLOG is installed, the /TASK switch  will  start  up
          task  accounting.   System  accounting must already be running



                                                                 PAGE 13



          with /UQIO enabled.  The /TASK switch should be a  command  by
          itself.  Once it is issued, TSKLOG will prompt for the user to
          input a list of task names which  are  to  be  accounted  for.
          TSKLOG  will  stop requesting tasks if a null line is entered.
          Only enter tasks which are going to exit.  A  task  accounting
          packet  is  not  logged  until the task exits.(task accounting
          starts when the task becomes active).  Tasks  like  MCR  which
          stop  themselves  are  always  active and can not be monitored
          short of aborting them.  Aborting a task  will  cause  a  data
          packet  to be sent, but aborting privleged exec tasks to moni-
          tor them is highly risky.  Task accounting may be  stopped  by
          issuing  either  the /NTASK or /STOP command.  THE /NTASK com-
          mand stops just task  accounting  whereas  the  /STOP  command
          stops everything.


          /PRINT, /NPRINT

               At times it is far more convenient to have data displayed
          directly  on the user's terminal than to have it sent off to a
          log file.  The /PRINT switch will disable sending task logging
          data  to  LOGTSK  and  will  enable  printing this data on the
          user's TI:.  Note, that while  TSKLOG  is  printing  the  task
          could  start  up  again  and TSKLOG would miss its start.  The
          /NPRINT switch disables printing to the user's  TI:,  and  the
          data is again sent off to LOGTSK.


          /SPOOL, //NSPOOL

               If one is using the new print  spooler/Queue-manager,  it
          is  possible  to log the total number of pages printed and the
          number of copies made on each print job.  Do to the complexity
          of  the  Queue-manager/print  spooler  the user account number
          will only be logged with the  spool  packet  if  the  user  is
          logged  on  at  his TI:  when the job is printed.  A user with
          print spooler sources and some time to  kill  could  file  the
          user  account number to disk along with the print job and then
          send it off to the print despooler along with the files to  be
          printed  instead of sending the terminal ucb address.  This is
          not hard to do but its implementation is defferred  until  the
          print  spooler  has  stabalized  and  I  have  access  to  the
          up-to-date Queue-manager sources.   Since  the  Queue  manager
          sources  are  not  distributed, this feature is implemented by
          replacing an object module in LPP.OLB.  The switch /SPOOL  en-
          ables logging print spooler statistics, and the /NSPOOL switch
          disables the logging.


     SYSLOG

          SYSLOG has three primary functions;  1) inserting  hooks  into
     the  exec  for a PIC code node in pool to use, 2) periodically log-



                                                                 PAGE 14



     ging system globle variables, 3) restoring the  EXEC  and  Pool  to
     virgin  condition on exit.  When SYSLOG is requested to run by ACC,
     it allocates a pool block and reads into  it  the  accounting  code
     (PIC).   It  then  intercepts the instructions at various points in
     the EXEC and replaces them with hooks into(ie  branches  into)  the
     appropriate  locations  in  the  code node.  Once the code node has
     been hooked into the EXEC the system will run  even  if  SYSLOG  is
     aborted.   Following  an  abort,  the  code  node may be removed by
     starting up SYSLOG again.  It will find its  code  node  and  start
     running.  At anytime thereafter, SYSLOG may be normally stopped and
     the dynamic memory it is using reclaimed.

          Next, SYSLOG uses the schedule interval passed on from ACC  to
     issue  a marktime.  It then issues a receive data or stop.  ACC can
     awaken SYSLOG by either sending a change scheduling interval packet
     ,  or a stop accounting packet.  The marktime also will awaken SYS-
     LOG.  When this happens, the variables consistent with the  setting
     of  the  system  accounting  mask are sent to the logging task, and
     then SYSLOG stops itself to wait for something else to happen.

          If memory and pool utilization accounting is selected,  SYSLOG
     becomes  careful  of  sending out data packets to LOG....  If total
     free pool drops below 200(10) words it does not send out the  pack-
     et.   In  this  case  it  does increment a counter to show how many
     times it wanted to send out a packet and there was too little pool.
     The  next  time  a packet is sent out this value will be sent along
     with it.

          When it is time to exit, SYSLOG will replace in the EXEC those
     instructions  which  were overwrittten when the hooks were inserted
     and will remove the code node from pool.   When  SYSLOG  exits  the
     system  returns  to the identical state it was in before SYSLOG was
     started.

          Inserting and removing hooks into the EXEC  is  a  rather  non
     standard  way of using a privleged program.  However, it has a sig-
     nificant advantage over any other method, namely that there is  ab-
     solutely  no  overhead  added  to  the  system unless accouniing is
     started.

          If the user selects that task accounting is desired, an  addi-
     tional two instructions are placed in the clock ISR routine, and if
     /UQIO is enabled the QIO intercept code adds a count  to  the  task
     account  control block QIO counter for every qio (if an accountable
     task is found).  If task accounting is not enabled, only  an  addi-
     tional  2 instructions of overhead are executed for a syslog assem-
     bled for task accounting.


     LOGTSK

          LOGTSK(LOG...) is an F4P program which receives data sent from
     TSKLOG, SYSLOG, ...HEL, HELTnn, ...BYE, BYETnn, ...UPD, and UPDTnn.



                                                                 PAGE 15



     if the sample interval is less than 5 minutes, it stops  itself  to
     wait  for  data.  It the interval is longer, it exits after logging
     each packet(s).


     HELLO

          HELLO is modified(above and beyond the normal KMS Fusion  mod-
     ifications)  slightly.   First  it  reads the user's account number
     from  the  account  file(RSX11.SYS)  into  a  word(U.ACN)  in   the
     terminal's  UCB.  The account number is used so that a later report
     program reading both the SYSLOG.DAT file and RSX11.SYS  can  deter-
     mine  who  was  sitting  on what terminal(very useful if one wishes
     ever to do charge back accounting).  The account number(and session
     ID)  are inserted into the account file using ACNT and implementing
     one of the conditionals existing for RSX11M-PLUS.  New account file
     offsets  must also be defined in ACTFIL.MAC.  Just prior to insert-
     ing the account number into U.ACN, HELLO  saves  the  value  stored
     there.   The  value stored there is the number of illegal or unsuc-
     cessful login attempts at that terminal since the last  logoff.   A
     very  security conscious system might be interested in this number,
     and it was essentially free.  Each time HELLO fails  to  log  on  a
     terminal this number is incremented.  

          Once U.ACN is inserted, all the counters in the user's UCB are
     reset  to zero, and a data packet sent of to LOG...  containing the
     logon time the account number, the terminal  number,  the  terminal
     type(TT:   or  VT:), the number of unsuccessful login attempts, and
     the login UIC.  It must be noted that a data packet is only sent to
     LOG...   if  the proper bit is set in $ACMSK.  In addition, the ac-
     count file is marked with the terminal flag to show  which  account
     is  on  which terminal(both for TT:  and VT:).  This enables BYE to
     later find out who is logging off.

          If the user still wishes to use the HELLO modifications  with-
     out doing the system generation required for system accounting, all
     the KMS features except system accounting may be obtained by  task-
     building  HELLO  with  a global definition for $ACMSK.  KMSGEN pro-
     vides information on how to select this option.


     BYE

          At logoff BYE finds the account entry in  RSX11.SYS  based  on
     the terminal number logging off and its terminal type.  It then up-
     dates the account file with the terminal connect time  in  minutes,
     and  the  CPU time in seconds.  If the proper bit is set in $ACMSK,
     it then sends off a data packet to LOG...  consisting of the  time,
     the  account  number, the terminal ID, the logoff uic, the CPU time
     used, and the number of QIO's issued.  If user  QIO  accounting  is
     not  enabled,  this  last value will be zero.  Whether or not it is
     enabled can be determined from other SYSLOG.DAT records.   Finally,
     the  UCB counters are reset to zero, the terminal logged off and if



                                                                 PAGE 16



     so requested by a bit in the user's terminal  privlege  mask  word,
     UPD  is requested to update the user's disk block usage.  Right be-
     fore BYE exits it prints out a summary of the user's connect  time,
     CPU  time,  and the number of tasks run.  BYE may also be assembled
     on a system not wanting system accounting by means of a global  de-
     finiton for $ACMSK.


     ACCLOG

          ACCLOG  provides  a  readout  of  the  system   account   file
     RSX11.SYS.   It  provides  a quick way of viewing the current total
     logon time, the total CPU time, the account number, the total files
     in  use  and  the disk blocks in use.  It additionally displays the
     percent of CPU utilization as a percent of the  total  logon  time.
     The interpretation of this number will vary depending on the number
     of terminals present and the average number logged on  at  any  one
     time.   The  task RESET is used to reset the cumulative time totals
     at some regular interval so as to start a new accounting period.


     UPD

          UPD scans through the user's SY:  and login uic,  tallies  the
     number  of  files  used and the number of disk blocks used, updates
     RSX11.SYS with this information and then if the proper bit  is  set
     in  $ACMSK, sends off a packet to LOG...  containing the disk block
     usage statistics.


     TSKLOG

          TSKLOG uses a lot of the code originally included as  part  of
     Greg  Basset's  ACCLOG.  It however, only controls part of the exec
     intercept code, namely that code involved with catching  the  start
     and  exit  of a task, and in catching each context switch to see if
     an accountable task is present.  Since a linked list  of  task  ac-
     count  blocks  must be scanned each context switch, this option can
     impose a lot of overhead if the list of tasks is  long.   For  this
     reason, it should be considered primarily as a performance measure-
     ment tool.  

          TSKLOG is currently not as intelligent as SYSLOG.   If  it  is
     aborted,  the system will probably still keep running, but the pool
     it used for the task accounting blocks and its code node  will  not
     be  reclaimed by running it again.  Only rebooting will recover the
     lost pool.  Hence it is very good practice  not  to  abort  TSKLOG.
     Also note that 10.  words of pool are used up for each task entered
     to be accounted for.  This could add up very rapidly if  a  lot  of
     tasks  were  entered.   Again  I emphasize that TSKLOG will degrade
     system performance if there is a lot of QIO activity.

          TSKLOG makes use of the information provided  by  SYSLOG,  and



                                                                 PAGE 17



     requires  SYSLOG  to  be  active  to  work.  However if SYSLOG were
     aborted TSKLOG would continue merrily on  its  way,  using  up  CPU
     time,  measuring  nothing, but not crashing.  However, it is consi-
     dered very bad practice to remove a task which TSKLOG has been told
     to  account  for.   When TSKLOG is given the list of tasks, it gets
     the TCB address for each task.  All kinds of things might happen if
     an  installed  task were removed and reinstalled with a new TCB ad-
     dress.  

          The ambitious user will note that TSKLOG  implicitly  provides
     hooks  for  computing the amount of memory used by a task(excluding
     regions) at each context switch.  If one did not worry about overh-
     ead,  it  would  be simple to calculate the kilocore-tics each user
     was using at each context switch.  Unfortunately, it would mean in-
     serting  the context switching code into SYSLOG and computing kilo-
     core-tics every context switch.  It could be done, but I doubt  its
     usefulness.

          The ambitious user should also note that while TSKLOG is  run-
     ning  two  useful side affects are present.  A two word tic counter
     is kept and is readable by any privileged task($TIME), also the ad-
     dress of the current task accounting block is at $TKBLK.  The exis-
     tence of a two word absolute time counter(if only $ABTIM  were  two
     words but that is another exec mod) allows privileged tasks to time
     critical routines without the overhead of the GTIM$ directive.   By
     storing the current task acounting packet in $TKBLK additional exec
     intercept code may be implemented  substantially  increasing  those
     parameters tasks are accounted for.



                                                                 PAGE 18



     IMPLEMENTING THE KMS SYSTEM ACCOUNTING PACKAGE



          At first it may seem to you that there are an  immense  number
     of changes to be made to DEC software.  While it is true that there
     are a large number of changes which eventually might be useful, all
     changes  do  not have to be made at once at the first SYSGEN.  Only
     one SYSGEN need be done.  

          All the SLP files were created(with the exception of ACNT.SLP)
     to be as independent of subsequent DEC SLP correction files as pos-
     sible.  The correct location in each file is  determined  using  an
     ASCII  locator  string  rather than a line number.  So if a DEC SLP
     file does not wipe out a locator, the SLP files should be  applica-
     ble  even  to  a  module which has been SLPED using a DEC SLP file.
     However, after applying a SLP file it  is  good  practice  to  read
     through  the  resultant file to see if something went really banan-
     nas.  These modifications have been through a large number of  SYS-
     GENS,  and unless something wierd is going on, they are rock solid.
     Almost the only thing which can be done wrong is forgetting to  SLP
     one of the files.


     Step by Step Instructions


     1.

          Rename the following files(this protects you from ever purging
     a distribution file).
     On the Executive Source disk (RK05 based systems) on [11,10],
     	TDSCH.MAC --> TDSCH.VGN
     	SYSCM.MAC --> SYSCM.VGN
      
     On [200,200] the following command files(Exec source disk)
           SGNTT.CMD   --> SGNTT.VMD
           SGNEXEC.CMD --> SGNEXEC.VMD
           SGNPER.CMD  --> SGNPER.VMD
      
     On [1,24]    replace JOBEND.OBJ in LPP.OLB(ON PRIVOBJ disk)
     	LBR JOBEND.VOB = LPP/EX:JOBEND
     	LBR LPP/RP=JOBEND
      
     On [200,200] of the baseline disk(or where ever you do your SYSGEN
      from)
            SYSGEN.CMD --> SYSGEN.VMD
      
     Place TDSCH.SLP, and SYSCM.SLP on [11,40] of the Exec  Source  disk
     and  SLP  the  files.   Next,  place  SGNPER.SLP,  sgnexec,slp  and
     SGNTT.SLP on [200,200] of the Exec source disk and SLP those files.
     Finally on whatever disk SYSGEN.CMD is located, place SYSGEN.SLP on
     [200,200] and SLP @SYSGEN.SLP.



                                                                 PAGE 19



     2.

          Do  a  SYSGEN.   Somewhere  on  this  kit  is  a  file  called
     SYSGENZ.CMD.   It  can be used as a prototype for any simple SYSGEN
     done in the future.  If you decide in advance what  tasks  you  are
     going  to build, and what options you want and configure your build
     disks appropriately, SYSGEN can run unattended and runs very  fast.
     However,  at  this  time do not worry about this.  Just keep in the
     back of your mind that there is an easier way to go for most user's
     than SYSGEN2 for the final phase of SYSGEN.

          Another item to keep in the back of your mind  is  that  else-
     where  on  this  kit are files which allow all of the utilities and
     many of the exec privleged tasks with an FCS resident library.   If
     you  want  to do this, you might just leave yourself a 4K partition
     for FCSRES during the current SYSGEN.


     3.

          VMR the target system and test it throughly to convince  your-
     self  it  is  solid.  It will be, the data structure changes should
     not affect anything.


     4.

          Apply ACNT.SLP to [15,10]ACNT.MAC on the MCR source disk.   As
     a  matter  of practice I always rename my distribution file to .VGN
     so it doesn't get purged.  The SLP file enables  certain  parts  of
     condtional  code  used by M-PLUS but which work just fine on RSX11M
     if some definitions are added to ACTFIL.MAC.  ACNT.OBJ must be  re-
     placed in MLTUSR.OLB on [1,24] of PRIVOBJ.  If you already have in-
     serted the KMS ACTFIL.OBJ you can rebuild ACNT immediately.  If not
     you  should  perform  use  @KMSGEN.   (You  must  use  the supplied
     ACTFIL.MAC for rebuilding ACNT.)


     5.

          Now you may use KMSGEN.CMD to  correctly  build  everything.(I
     think.)


     6.

          Test everything out.  Replace any modified modules in the  ap-
     propriate object module libraries.  Be sure all is ok for next SYS-
     GEN you do.  Write me and let me know how it went and  what  should
     be done to make it simpler or what features are needed.


     7.



                                                                 PAGE 20



          SYSLOG.HLP is a HELP file which will tell you how to use  SYS-
     LOG, ACC, TSKLOG, and LOGTSK.  IN addition it defines the structure
     of the accounting data packets.  Read the HELP information.   Write
     a  nifty program to analyize SYSLOG.DAT in some particular fashion.
     Pass the program around to other users(like  me)  who  haven't  had
     time to write a fancy analysis program yet.  At present only ACCLOG
     and CPUREP are provided as reports.








                                                                            PAGE 21



					TABLE II
 
			FORMATS OF DATA PACKETS SENT TO LOG...
 
	WORD 1								  WORD 13
 
	RECTYP
        -------------------------------------------------------------------------
START	!  1  !HR!MIN!SEC! YR  ! MO  ! DAY ! TIC ! TPS !DELTA!  *  !  *  !$ACMSK!
	-------------------------------------------------------------------------
STOP	! -1  !HR!MIN!SEC! YR  ! MO  ! DAY ! TIC ! TPS !DELTA!TKNM1!TKNM2!$ACMSK!
	-------------------------------------------------------------------------
GLB	!  2  !HR!MIN!SEC!NULL1!NULL2!SHFCT!CKPCT!LDRCT!QICT1!QICT2!RUNCT!  *   !
	-------------------------------------------------------------------------
MEMORY	!  3  !HR!MIN!SEC!NTSKS!TKMEM!NCKP !CKMEM!TPOOL!LGFRG!NFRAG!NTSNT!  *   !
	-------------------------------------------------------------------------
DELTA	!  4  !HR!MIN!SEC! YR  ! MO  ! DAY ! TIC ! TPS !DELTA!TKNM1!TKNM2!$ACMSK!
	-------------------------------------------------------------------------
HELLO	!  5  !HR!MIN!SEC!TRMID!ACNT ! UIC !NILEG!  *  !  *  !  *  !  *  !  *   !
	-------------------------------------------------------------------------
BYE	!  6  !HR!MIN!SEC!TRMID!ACNT ! UIC !CPU1 !ATCNT!QICT1!QICT2!RUNCT!INSCNT!
	-------------------------------------------------------------------------
UPD	!  7  !HR!MIN!SEC!ACNT !SYSDV(2WDS)!NFILE!NBLKS!ABLKS!  *  !  *  !  *   !
	-------------------------------------------------------------------------
CO: PKT	!  8  !HR!MIN!SEC!  0  !  0  !  0  !CPU1 !CPU2 !QICT1!QICT2!RUNCT!  *   !
	-------------------------------------------------------------------------
TSK PKT	!  9  !HR!MIN!SEC!ACNT !CLK1 !CLK2 !CPU1 !CPU2 !QICT1!QICT2!  *  !  *   !
	-------------------------------------------------------------------------
SPL PKT ! 10  !HR!MIN!SEC!ACNT !TOTPG!COPYS!  *  !  *  !  *  !TKNM1!TKNM2!  *   !
	-------------------------------------------------------------------------
 
 
	RECTYP	-1 - 99	RESERVED
		100-	USER USABLE



                                                                            PAGE 22



			   SYMBOL LEGEND FOR TABLE II
 
 
	HR	- HOUR OF DAY
	MIN	- MINUTE OF HOUR
	SEC	- SECOND OF MINUTE
	YR	- YEAR OF UNIVERSE
	MO	- MONTH OF YEAR
	DAY	- DAY OF MONTH
	TIC	- TIC OF SECOND
	TPS	- NUMBER OF TICS/SEC OF CLOCK
 
	$ACMSK	- SYSTEM ACCOUNT FEATURE MASK
	ABLKS	- MAXIMUM BLOCKS ALLOWED ON SYSTEM DEVICE
	ACNT	- USER ACCOUNT NUMBER
	CKMEM	- TOTAL MEMORY REQUIRED FOR ALL CHECKPOINTED TASKS
	CKPCT	- NUMBER OF CHECKPOINT REQUESTS
	CLK1	- WALL CLOCK RUN TIME(LOVAL)
	CLK2	-   "    "    "    " (HIVAL)
	COPYS   - NUMBER OF COPIES PRINTED IN JOB
	CPU1	- CPU TIME USED(LOVAL)
	CPU2	-  "    "   "  (HIVAL)
	DELTA	- SAMPLE INTERVAL IN MINUTES
	LDRCT	- NUMBER OF LOADER REQUESTS
	LGFRG	- SIZE OF LARGEST POOL FRAGMENT
	NBLKS	- TOTAL NUMBER OF DISKS BLOCKS IN USE AT LOGOFF
	NCKP	- NUMBER OF TASKS CHECKPOINTED
	NFILE	- NUMBER OF USER FILES AT LOGOFF
	NFRAG	- NUMBER OF POOL FRAGMENTS
	NTSKS	- NUMBER OF TASKS IN CORE
	NTSNT	- NUMBER OF TIMES SYSLOG DID NOT SEND DATA BECAUSE POOL LOW
	NILEG	- NUMBER OF ILLEGAL LOGIN ATTEMPTS
	NULL1	- TIME IN IDLE LOOP(TICS) - LOVAL
	NULL2	-   "  "   "    "    "    - HIVAL
	QIOCT1	- NUMBER OF QIO'S ISSUED(LOVAL)
	QIOCT2	-    "   "   "      "   (HIVAL)
	RUNCT	- NUMBER OF RUN REQUESTS
	SHFCT	- NUMBER OF SHUFFLER REQUESTS
	SYSDV	- USER'S SYSTEM DEVICE(FORMAT TBD)
	TKMEM	- AMOUNT OF FREE CORE IN USE BY TASKS
	TKNM1	- SENDER/REQUESTER TASK NAME(RAD50)-FIRST PART
	TKNM2	-   "       "       "    "    "    -SECOND PART
	TOTPG	- TOTAL NUMBER OF PAGES PRINTED IN JOB
	TPOOL	- TOTAL SYSTEM POOL
	TRMID	- TERMINAL ID(HI BYTE-'T' OR 'V', LO BYTE-UNIT NUMBER)
	UIC	- USER'S LOGIN UIC
	  *	- RESERVED FOR FUTURE USE