MSX (MULTI SYSTEM EXECUTIVE) MULTI-TASKER

	MSX IS A MULTITASKING SCHEME THAT RUNS USING DOS OR RSX IN CORE
BUT DOING SOME OF ITS OWN I/O. IT LOOKS LIKE A MAIN PROGRAM TO DOS OR RSX
AND IS RUN LIKE A MAIN PROGRAM. HOWEVER, ONCE STARTED IT HANDLES
THINGS MORE OR LESS INDEPENDENTLY OF ANY UNDERLYING OPERATING SYSTEM.
IN PARTICULAR, MSX CONTROLS STACK ALLOCATION.
	TASKS ARE DEFINED BY A TASK TABLE (ALL ARE CORE-RESIDENT OR
THE USER DOES HIS OWN SWAPPING, POSSIBLY VIA TKB'S OVERLAY
STRUCTURES)WHICH TELLS MSX WHAT STATE TASKS ARE IN. SYSTEM
DIRECTIVES (TRAP CALLS) TELL MSX WHAT TO DO.
	THE MSX SYSTEM OCCUPIES 12-14K OF MEMORY IN ITS RSX
VERSION, PLUS WHATEVER IS NEEDED FOR TASK TABLES. REMAINING
SPACE IS THE VIRTUAL ADDRESS SPACE AVAILABLE PER TASK. THE STAND
ALONE SYSTEM'S CORE NEEDS ARE COMPARABLE TO THIS; HOWEVER, SINCE
STAND-ALONE MSX IS ALSO A MAPPED SYSTEM (WHICH COULD BE CHANGED VIA
SOME ADDITIONAL ASSEMBLY CONDITIONALS), THE STAND-ALONE SYSTEM 
LEAVES 32K FOR EACH TASK, IN USER SPACE, AND HAS ROOM IN THE TCB 
TO STORE DATA PARS TO PERMIT I/D SPACE SEPARATION IF DESIRED 
IN USER MODE.
	STAND-ALONE MSX HAS A VERSION OF DDT NORMALLY AVAILABLE FOR
DEBUGGING AT SYSTEM LEVEL, ENTERED WHENEVER ONE TYPES CONTROL-T TO
THE CONSOLE HANDLER ON INPUT, AND ON BREAKPOINTS. THIS MAY BE REMOVED
ONCE THE SYSTEM IS WORKING. EVERY CPU IN MSX CONTAINS A COPY OF MSX
WITH INITIALLY IDENTICAL TASK TABLES. WHERE NO DYNAMIC LOADING IS
PRESENT TASKS ARE ALSO PRESENT; OTHERWISE, A NAMELIST IN MXSUBS IS
PRESENT GIVING TASK NAMES AND DISK LOCATIONS, AND SOME "EMPTY"
TASK CONTROL BLOCKS (TASK NAME = 177775 OCTAL) ARE PRESENT IN EACH SYSTEM.
	THE SYSTEM TASK LIST (STL) AND EACH TASK CONTROL BLOCK (TCB)
THAT IS AN ENTRY IN THE STL, ARE THE KEY DATA STRUCTURES FOR MSX TASKS.
THESE ARE SET UP VIA THE TCB MACRO DEFINED IN MXSTLS.MAC.

FILE		FUNCTION

MXSCNS		MAIN PROGRAM AND TASK SCANNER
		ALSO MOST OF INPUT MESSAGE HANDLER FROM OTHER CPU'S
		AND CLOCK SERVICES.
MXTRPS		TRAP HANDLER FOR MSX DIRECTIVES
MXTBLS		TABLES; CONTROL TABLE; INTERRUPT VECTOR SAVE TABLE;
		FREE SPACE TABLE; LOGICAL UNIT TABLE
MXCODS		INTERRUPT POSTING; INTERRUPT VECTOR SAVE/RESTORE,
		IOT HANDLER, REG. SAVE/RESTORE
MXIOHT		BASIC, REQUIRED QTRAN PROCESSOR IF ANY QTRAN I/O
		IS DONE. RE-ENTRANT.

MTIOHT		MAGTAPE HANDLER TASK (DOS)
KBIOHT		KEYBOARD (CONSOLE) I/O HANDLER. (DL11)
DTIOHT
DT		DECTAPE HANDLER (EXAMPLE OF 18 BIT DMA DEVICE HANDLER)
VTIOHT
CRIOHT
DFIOHT
LPIOHT
LP		LINEPRINTER HANDLER
		I/O HANDLER TASKS FOR QTRAN TO VARIOUS DEVICES.
MXKBDRV		STAND ALONE KEYBOARD DRIVER
MXLPDRV		STAND ALONE LINEPRINTER DRIVER
MXDTDRV		STAND ALONE DECTAPE DRIVER
MXSTLS		SYSTEM TASK LIST TCB DEFINER MACRO AND STL ITSELF
		ALSO SOME SYSTEMWIDE TABLES AND THE CPU NUMBER
		OF THE SYSTEM (MX.CPU).
MXSUBS		COMMON SUBROUTINES FOR MSX SUPPORT. ALSO LOADER
		SUPPORT AND MLS SUPPORT.
MXCONN		INTERPROCESSOR CONNECTION PRIMITIVES THAT MUST BE
		CUSTOM SUPPLIED FOR ANY GIVEN SYSTEM ARCHITECTURE.
		THIS MODULE MUST BE REDONE FOR EVERY SYSTEM CONNECTION;
		A VERSION PRESENTLY DONE IS FOR RSX MODE WITH INTER
		CPU COMMUNICATION EMULATING A GLOBAL BUS VIA A COMMON
		MEMORY AREA.
MXMAP		ROUTINE TO SET UP INITIAL MAPPING
MXWDMG		APR REMAPPING CODE FOR RSX BASED MSX VERSIONS THAT DO
		MEMORY MAPPING.
MXINTS		RSX BASED MSX INTERRUPT INTERFACING CODE EXAMPLE.

	FOR RSX VERSIONS, MXIOHT AND ALL IOHT TASKS ARE ABSENT. CODE IN
MXTRAP HANDLES I/O VIA THE QIO$ DIRECTIVE, WITH MULTIPLE REQUESTS PER
LUN QUEUED IN THE SYSTEM. IT WILL NORMALLY BE TRUE THAT TASKS WILL QUEUE
THEIR REQUESTS ON INPUT AND A SPECIAL TASK WITHIN MSX WILL HANDLE I/O
TO DISKS, TAPES, ETC., BUT THE QTRAN DIRECTIVE WILL ENSURE THAT ALL
I/O SEEN BY RSX IS QUEUED EVEN IF MULTIPLE REQUESTS ARE OUTSTANDING BY
POSSIBLY MORE THAN ONE TASK.
	THE STAND-ALONE VERSION OF MSX SUPPORTS DEVICES KB (INPUT AND
OUTPUT, FULL-DUPLEX), LP, AND DT. THE VERSION OF 8-JUN-1979 INCLUDES
18-BIT ADDRESSING SUPPORT FOR THESE. 22-BIT SUPPORT IS EASIEST IN THIS
CASE WITH STATIC ALLOCATION OF UMR'S (E.G. ON 11/70 OR 11/44).

	MEMORY MAPS ARE AS FOLLOWS:

	FOR THE DOS-11 VERSION:

	TOP	OF	MEMORY

	TASKN
	..........................
	TASN N-1
	..........................
		.
		.
		.
	..........................
	TASK 2
	..........................
	TASK 1
	..........................
	MSX SCHEDULER
	..........................
	DOS DRIVERS, DDB'S, ETC.
	..........................
	DOS-11
0	..........................


	FOR THE RSX VERSION:

	.............................................................
APR 7	I/O PAGE DEVICE COMMON (R/W ACCESS TO ALL OF I/O PAGE)
	.............................................................
APR 6	COMMON TASKS (PAGES OF COMMON ROUTINES)
	.............................................................
APR 5	DATA AREAS (EACH TASK HAS ITS OWN MAPPING)
	.............................................................
APR 4	DATA AREAS (EACH TASK HAS ITS OWN MAPPING)
	.............................................................
APR 0	MSX SCHEDULER, TASK TABLES, MAPPING CONTROL ROUTINES
TO WHATEVER IS NEEDED. MSX REMAPS ALL APRS FROM 1 THRU 6
PER TASK, BUT NOT ALL ACTUALLY CHANGE PER TASK.
	.............................................................



	FOR THE STAND-ALONE, DUAL MODE VERSION:

		KERNEL SPACE
	.............................................................
APR 7		I/O PAGE
	.............................................................
APR 6

THRU

APR 0

	DDT, MSX SCHEDULER, TABLES, DRIVERS
	.............................................................


		USER SPACE

	.............................................................
APR 7	INITIALLY I/O PAGE
	.............................................................
APR 6

THROUGH		DATA/PROGRAM AREAS

APR 1
	.............................................................
APR 0	MSX TASK ENTRY POINT AREAS (APR 0 ALWAYS SET UP SAME AT
		TASK STARTUP)
	.............................................................

	NOTE THAT IN USER SPACE, PREVIOUS MODE IS ALWAYS KERNEL, AND
	A TASK'S MAPPING IS PROPAGATED AS LONG AS IT RUNS (AND TENDS
	IN THE STANDALONE VERSION TO REMAIN PROPAGATED EVEN AFTER
	EXIT AND RE-REQUEST)
		IN USER MODE, MSX WILL NORMALLY SET UP ALL APRS TO
INITIAL VALUES SPECIFIED IN THE TCB MACRO OR BY MXMAP.



	SPECIAL ENTRIES INTO MXTRAP ALLOW FOR A TASK TO REQUEST ANOTHER
TASK DIRECTLY BY NUMBER OR NAME, OR TO EXIT, WITHOUT GOING THROUGH THE
FULL TRAP DECODING LOGIC. IF THE TASK IS SPECIFIED BY NUMBER, MOST OF
THE LOOKUP OVERHEAD MAY BE BYPASSED ON REQUEST (OR RESUME).

	TO DO RSX CALLS, THE TRAP INSTRUCTION IS SLOW SINCE IT IS
AN SST. HENCE, SUBROUTINE ENTRIES ARE PROVIDED INSTEAD. THE TRAP
SEQUENCES WILL WORK A LA DOS VERSION, BUT THE SUBROUTINE CALLS ARE
FASTER.
	THERE ARE 2 SUBSTITUTE SEQUENCES. THE FIRST IS

	(PUSH ARGUMENTS FOR CALL ON STACK)
	JSR	PC,MX.SVC	;CALL TRAP SERVICE
	.WORD	TRAPCODE	;CODES ARE 0,1,2,3,4,5,6,7,10

	THE SECOND IS SLIGHTLY FASTER:

	(PUSH ARGUMENTS FOR CALL ON STACK)
	JSR	PC,MX.SV2	;CALL TRAP SEQ. WITH DOUBLED CODES
	.WORD	TRAPCODE+TRAPCODE ; THUS, 0,2,4,6,8,10,12,14,16

	FOR REQUEST AND EXIT, THERE ARE IN ADDITION THE FOLLOWING
ALTERNATIVES, FOR SPEED...
 REQUEST (REQPRI):
	(PUSH REQUEST ARGS ON STACK)
	CLR	-(SP)	;FAKE A PSW
	JSR	PC,MX.PRR	;PRIORITY REQUEST

 EXIT
	MOV	#EV,-(SP) ;PUSH A 0 OR EV ADDR
	CLR	-(SP)	;FAKE PSW
	JSR	PC,MX.PRX	;SCRAM FASTER




	TASK TABLE DEFINITION
MSX FINDS THE TASK TABLE, WHICH TELLS  OF USER TASKS, STATES, AND
PRIORITIES, BY THE GLOBAL "MX.TBL". THIS MUST BE THE FIRST
WORD OF THE TABLE AND BE DECLARED GLOBAL. ONE EASY WAY TO
DO SO IS TO CODE THUS:

	.TITLE	MSXTBL
	.PSECT	MX.TBL,D,GBL,RW
	.GLOBL	MX.TBL
MX.TBL:
	(ENTRIES.)
	.GLOBL	MX.TBE
MX.TBE:
	.WORD	0	;TERMINATOR FOR TABLE. REQUIRED.

	EACH ENTRY IS 16 (32 IN STAND-ALONE) WORDS LONG, LAID OUT
AS FOLLOWS:

ENTRY:	.RAD50	/NAM/	;TASK NAME
	.BYTE	PRI	;PRIORITY. (IGNORED NOW; PRIORITY
				IS DETERMINED BY TABLE POSITION, HIGH
				PRIORITY TASKS BEING THE FIRST ONES.)
	.BYTE	STAT	;STATUS OF TASK. CURRENT STATE (0-4) IS SET
				;BY SYSTEM HERE. INITIALLY VALUES MUST
				;BE SET BY USER FOR INITIAL TASK
				;CONTROL.
	.WORD	BEGINADDRESS	;TASK START ADDRESS
	.WORD	ISP	;INITIAL STACK POINTER. (MUST BE A POSITION NOT
				;USED ON STACK BY TASK. MSX USES TOP WORD,
				;THOUGH IN NORMAL DOS OPERATIONS IT WOULD
				;NOT BE USED.)
	.WORD	DSP	;DYNAMIC STACK POINTER. (SP WHEN TASK IS NOT
			;RUNNING AND NOT IN STATE 0)
	.WORD	CSP	;CHECK STACK POINTER. SUPPOSED TO LET MSX CHECK
			;INDIVIDUAL STACK OVERFLOW. CURRENTLY UNUSED.
	.WORD	0	;ADDRESS IN MSX OF TABLE OF INITIAL APRS, F.P.
			;REGS, AND TASK TRAP ADDRESSES.
	.WORD	EVA	;EVENT VARIABLE ADDR FOR WAITS AND ORWAITS.
	(AN ADDITIONAL 24 WORDS FOR A TOTAL OF 32 ARE INCLUDED IN
	THE STANDALONE MSX TABLES FOR REGISTER, PC, AND APR SAVES)
	;THE MSX TABLE CONTAINS 8 WORDS FOR REGISTERS, PC, AND PS
	;FOR STANDALONE VERSIONS (IN RSX VERSIONS, THIS IS IN THE
	;STACK), AND 8 FOR APRS. IN ADDITION, 8 WORDS ARE USED
	;TO POINT TO ADDITIONAL TABLES USED TO CONTROL THE TASK.
	;SEE MXSTLS FOR DESCRIPTION.


	NAME, STAT,BEGINADDRESS, AND ISP SHOULD BE SET
BY THE USER. STAT IS NORMALLY 0 IF TASKS ARE TO BE STARTED BY
REQUEST DIRECTIVES OR 4 FOR TASKS WHICH SHOULD BE GIVEN CONTROL UPON
STARTUP. AT LEAST 1 TASK, THE INITIALIZER, SHOULD BE SET AT
STATE 4.

	DON'T FORGET TO PUT A 0 AT THE END OF THE TABLE AFTER THE
LAST ENTRY TO MARK THE END OF THE TABLE.
	THE GLOBAL SYMBOL MX.TBE SHOULD BE DEFINED AFTER THE LAST STL
ENTRY, AND THE SYMBOL MX.TBS IS THE NUMBER OF BYTES IN A TASK TABLE
ENTRY (IT MUST BE A POWER OF 2) AND MX.CNT IS THE SHIFT COUNT FOR
CONVERTING A NUMBER (0,1,2,3,4,5,...) INTO AN OFFSET FROM MX.TBL
(FOR USE TO SPECIFY REQUESTING TASKS BY NUMBER STARTING AT 0 RATHER
THAN BY RAD50 NAME).

	IF TASKS ARE TO BE MAPPED IN VIA APR 1 IN A MAPPED
MSX, THE INITIAL CONTENTS OF APR 1 SHOULD BE SPECIFIED. IT MAY
BE ASSUMED FOR THE RSX VERSIONS THAT MSX RESIDES AT PHYSICAL
ZERO IN MEMORY; THE APR 1 VALUE WILL BE RELOCATED TO CORRESPOND TO
THE ACTUAL LOCATION AT RUNTIME.
	IF BIT 7 (THE 200 BIT) IS SET IN THE TASK STATUS AT ANY
TIME, THE MSX SCANNER WILL CONSIDER THE TASK DISABLED AND WILL
BYPASS IT IN ANY SCAN FOR WORK. THIS ALLOWS A TASK TO SUSPEND
ANOTHER TASK AS OF THE NEXT TIME THE OTHER TASK ISSUES A MSX
DIRECTIVE. CLEARING THIS BIT AND ISSUING A DECLARE (SEE BELOW)
WILL ALLOW THE TASK TO RESTART IF IT IS THE HIGHEST PRIORITY TASK
ELIGIBLE TO RUN.

	IN ORDER TO PROVIDE MAXIMUM SPEED TRANSFERS, MSX SYSTEM
TRANSFER PATHS ARE KEPT SHORT AND ORDERLY. SOME CARE IS NEEDED IN
THE SCHEDULER IF CERTAIN VALIDITY TESTS ARE CONDITIONALLY EXCLUDED
FROM ASSEMBLY, BUT THE MSX EXECUTIVE IS DESIGNED TO ALLOW EFFICIENT
USE OF THE CPU BY CO-OPERATING TASKS. IT DIFFERS FROM RSX IN THIS
PHILOSOPHY; WHEREAS RSX IS A MULTI-USER, MULTI-TASK SYSTEM, MSX IS
A SINGLE-USER, MULTI-TASK SCHEDULER. AS SUCH, IT ASSUMES SOME 
CO-OPERATION AMONG ITS TASKS. IN PARTICULAR, MSX MAY BE ASSEMBLED TO
ALLOW REQUESTS OF ALREADY ACTIVE TASKS (EFFECTIVELY A RESUME OR A
NO-OP), AND ITS TASK TABLES MAY BE ALTERED BY TASKS. THIS IS AN
EXTERMELY EFFICIENT WAY TO HANDLE SCHEDULING, AS TASKS MAY BE
ENABLED TO RUN BY SETTING THEIR STATUSES UP TO RUNNING AND THEN
REQUESTING THE FIRST. THE NORMAL PARTIAL SCAN WILL THEN RUN THEM
SEQUENTIALLY. TASKS MAY SHARE A STACK IF THEY NEVER CAN RUN
SIMULTANEOUSLY. 
	TO ALLOW FAST I/O RESPONSE, MSX HAS A MECHANISM FOR RSX
THAT PERMITS A TASK TO BE REQUESTED WHEN THE I/O COMPLETES. THIS
MEANS THE NORMAL WAITING FOR EVENT VARIABLE MECHANISM MAY BE
BYPASSED AND CONTROL TRANSFERRED DIRECTLY TO THE DESIRED ROUTINE
ON I/O DONE.
	THIS IS NOT ESPECIALLY DESIRABLE MUCH OF THE TIME, SO
STAND-ALONE MSX ALLOWS THE WORD BEFORE THE EVENT VARIABLE TO
CONTAIN AN "INTERRUPT" ADDRESS FOR USE ON I/O COMPLETION. THIS
WILL CAUSE A SIMULATED INTERRUPT ON I/O DONE. HOWEVER, NOTE
THAT THIS WILL NOT OCCUR IF A LIBRARY HAS BEEN ENTERED AND THE
"INTERRUPTS" MAY BE LOST IN THAT CASE. THIS IS DONE FOR SECURITY
REASONS.
	MSX MAY BE ASSEMBLED TO CHECK PRIORITY LEVELS AND START A
SCAN WITH THE HIGHEST PRIORITY TASK THAT HAS BEEN REQUESTED BUT
NOT EXITED. WHERE THE TASK LIST IS VERY LONG, THIS CAN SAVE TIME
AS 16 TASKS MAY BE TESTED AT ONCE AND SKIPPED IF NONE ARE ACTIVE.
THIS FEATURE IS NOT NORMALLY SELECTED SINCE THE DYNAMIC PRIORITY
SUPPORTED BY THE MSX AUXILIARY QUEUE CONFLICTS WITH IT.
	THE NORMAL I/O SCHEME UNDER MSX IS THE QTRAN DIRECTIVE,
WHICH TRANSLATES INTO A QIO$ UNDER RSX. IF THE TASK IS CHECKPOINTABLE,
RSX WILL SUSPEND THE TASK IF MORE THAN 1 I/O REQUEST IS PENDING ON
A LUN. MSX WILL OVERCOME THIS PROBLEM BY QUEUING I/O REQUESTS
INTERNALLY AND ISSUING THEM TO RSX 1 AT A TIME (PER LUN). IF THE
TASK IS NON-CHECKPOINTABLE (AS IT MUST BE TO DO MEMORY MANAGEMENT),
RSX WILL NOT SUSPEND THE TASK, AND THE INTERNAL QUEUING MAY BE
EXCLUDED BY CONDITIONAL ASSEMBLY. INTERNAL QUEUING MECHANISMS FOR
THE STAND-ALONE VERSION ARE SIMILAR IN CONCEPT, BUT NOT IN DETAIL.
	MSX ALLOWS MEMORY MAPPING BY CALLING SUBROUTINES TO ALTER
APR'S (PARS MAY BE ALTERED, BUT PDR'S ARE ASSUMED FIXED AND WILL
NORMALLY MAP 4K R/W REGIONS). UNDER RSX, IT DOES THIS BY CHANGING THE
PHYSICAL HARDWARE AND THE RSX MAPPING DATA TOGETHER (EXTRACTING
INFORMATION FROM RSX AT STARTUP ON THE LOCATIONS TO ALTER) IN
AN INSTRUCTION SEQUENCE OF 5-15 INSTRUCTIONS (DEPENDING ON THE
OPTIONS SELECTED FOR CHOOSING THE NEW ADDRESS). THE MSX TASKS
RUNNING UNDER RSX11M MAY OF COURSE ISSUE RSX DIRECTIVES, BUT THE
INTENT OF A QTRAN DIRECTIVE IS TO ENSURE THAT IF IT IS NECESSARY
TO BYPASS SOME RSX CODE TO SPEED UP I/O TO RSX DEVICES, THE
INTERFACE TO THE USER WILL BE TRANSPARENT. THE CURRENT IMPLEMENTATION
PROVIDES 7 LOGICAL UNITS THAT CORRESPOND TO 7 FILES ON THE DISK
IN ADDITION TO LUNS FOR CONSOLE, TAPE, ETC. THESE LOGICAL UNITS
(LUNS) ARE ACCESSED BY IO.RVB OR IO.WVB TO READ AND WRITE VIRTUAL
BLOCKS OF THE FILES; TO THE MSX TASKS, THEY MAY APPEAR TO BE
ENTIRE VOLUMES. HOWEVER, THEY WILL BE ON PROTECTED DISK AREAS
AND SAFE FROM OTHER RSX TASKS. THIS MECHANISM ALLOWS GREAT 
FLEXIBILITY IN HIGH-SPEED I/O OPERATIONS WITHOUT EXCESSIVE
DANGER TO THE REST OF THE HOST RSX SYSTEM. UNDER THE STAND-ALONE
VERSION, EACH LUN WOULD BE A PHYSICAL VOLUME. THESE FILES MAY
BE INCREASED IN NUMBER, BUT THE METHOD IS CHOSEN TO AVOID EXCESSIVE
DELAY FROM FILES-11 PROCESSING THAT CAN OCCUR DUE TO OPEN AND
CLOSE TIMES.
	IT SHOULD BE NOTED THAT THE USE OF RSX LUNS FOR FILES
IS CONDITIONALLY ASSEMBLED IN MSX AND PROBABLY WILL NOT BE USED
SINCE OPEN/CLOSE LOGIC IN RSX11M BRINGS IN ABOUT 2K OF CODE
IN ADDITION TO THE CONTROL BLOCKS USED. THEREFORE, QTRAN WILL
SIMPLY ISSUE THE RSX CALLS TO QIO$ AND HANDLE COMPLETION AST'S
WITH NO FURTHER ADO UNLESS AN EXTRA APR CAN BE SPARED FOR THE
FILE HANDLING. FILES MAY BE HANDLED VIA ANOTHER TASK MAPPING TO
THE SAME DATA REGION AS MSX.

	MSX IS SUPPLIED IN SOURCE FORM TO ALL WHO HAVE IT AND
MAY BE EASILY TAILORED TO A SPECIFIC SET OF NEEDS.



		LIMITATIONS

	ERROR INDICATIONS FROM MSX (ODD ADDRESS TRAPS,
ETC.) NORMALLY IN THE PRESENT VERSION WILL PRINT THE
ADDRESS OF THE FAULT, THE TASK NAME, AND THE CONTENTS
OF THE PAR FOR APR 1, THEN EITHER CONTINUE OR EXIT THE
SYSTEM. PROVISION FOR DUMPING DATA IS PRESENT IN RUDIMENTARY
FORM, BUT THE ERROR PROCESSING IS AT PRESENT MINIMAL AND
PRELIMINARY. THIS MAY BE FIXED WITH A LITTLE WORK AND SOME
IDEA WHAT IS WANTED. LINKING WITH DDT IS HOWEVER A GOOD
FIRST STEP AT ALLOWING A MORE SENSIBLE RECOVERY UNTIL A CUSTOM
METHOD IS AVAILABLE. SUFFICIENT INFORMATION TO ALLOW ERROR
RECOVERY TASKS TO RUN IS AVAILABLE TO THE ERROR LOGGER; THESE
ARE JUST NOT IMPLEMENTED. THE CONSOLE OUTPUT WILL LOOK A BIT
LIKE OLD DOS-11 OUTPUT; MSX WAS ORIGINALLY DEVELOPED TO
RUN USING DOS DEVICE DRIVERS AND HAD TO HANDLE THEIR IOT'S
FOR DEVICE UNREADY CONDITIONS. THESE HISTORICAL ARTIFACTS ARE
OF NO PRESENT CONCERN HOWEVER. NOTE THAT MSX DRIVERS, UNLIKE
THEIR DOS COUNTERPARTS, ACCEPT BYTE COUNTS RATHER THAN WORD COUNTS.

	MSX SYSTEM DIRECTIVES
NOTE:
	THE MACRO NAMES HERE ARE ONE SET OF CUSTOMARY ONES; THE
ASSEMBLY EXPANSIONS ARE IMPORTANT, BUT OTHER MACROS ARE POSSIBLE
(AND HAVE BEEN DEVISED) TO ALLOW EASIER CODING WHERE FEWER USER-
SPECIFIED ARGUMENTS ARE NEEDED.
	THE FOLLOWING ARE THE OLDEST AND MOST BASIC MSX SYSTEM
DIRECTIVES. FOR A FULL LIST, SEE MSX11.RNO.

	WAIT

		WAIT.	#EV	;WAIT TILL EV BECOMES NON-ZERO

ASSEMBLY:

	MOV	#EV,-(SP)
	TRAP	0

ACTION:

	TASK ENTERS STATE 2 AND STAYS THERE TILL THE WORD 
EV BECOMES NON-ZERO. ON RETURN, CONDITION CODES REFLECT
THE VALUE OF EV (EVENT VARIABLE) AT THE TIME OF THE TASK-SCAN.


	PRIREQ

		PRIREQ	#NAM,#PRI,#EV ;REQUEST HIGHER PRIO TASK DIRECTLY

ACTON:

	TASK IS DIRECTLY ENTERED WITHOUT A FULL SCAN, THOUGH A SIGNIFICANT
EVENT IS RECORDED FOR LATER. IF A HIGHER PRIORITY TASK HAS BEEN STARTED
BUT NOT EXITED, PRIREQ IS EXACTLY EQUIVALENT TO REQUEST. OTHERWISE IT
GOES TO THE TASK LOCATION WITHOUT A SCAN. NOTE THAT THE HIGHEST PRIORITY
TASK IS A WORD, NOT A LIST; IF TASKS ARE NESTED WRONG, THE LOGIC COULD OMIT
A SCAN SOMETIMES WHERE IT MIGHT BE ADVISABLE TO HAVE IT.

ASSEMBLY:
	MOV	#EV,-(SP)
	MOV	#PRI,-(SP)
	MOV	#NAM,-(SP) ;OR TASK NUMBER FROM 0
	TRAP	1

	ORWAIT

		ORWAIT	#EVTAB	;WAIT UNTIL ANY OF THE WORDS IN EVTAB
				;BECOME NONZERO

ASSEMBLY:

	MOV	#EVTAB,-(SP)
	TRAP	2

ACTION:

	TASK ENTERS STATE 3 AND REMAINS UNTIL ONE OR MORE OF
THE WORDS IN EVTAB IS NONZERO.

	THE FORMAT OF EVTAB IS:

	EVTAB:	.WORD	EV1
		.WORD	EV2
		.WORD	EV3
			.
			.
			.
		.WORD	0	;TERMINATOR

WHERE THE EVENT VARIABLES EV1, EV2, EV3,...,EVN ARE WORDS
IN MEMORY.

	SUSPEND

		SUSPEND	;STOP TASK UNTIL SOMEONE ELSE TELLS IT TO RESUME

ASSEMBLY:

	TRAP	3

ACTION:

	TASK ENTERS STATE 1 AND REMAINS UNTIL ANOTHER TASK ISSUES A
RESUME DIRECTIVE SPECIFYING THIS TASK.

	RESUME

	RESUME	#NAM,#RA,#EV

ASSEMBLY:

	MOV	#EV,-(SP)
	MOV	#RA,-(SP)	;RESUME ADDR
	MOV	#NAM,-(SP)	;TASK NAME TO RESUME
	TRAP	4

ACTION:

	THE TASK WHOSE NAME IS AT NAM IS RESUMED AT ADDRESS RA.
IF RA IS NOT SPECIFIED (IS 0), TASK NAM RESUMES AT THE
INSTRUCTION FOLLOWING THE SUSPEND IT ISSUED TO GET INTO
STATE 1. IF THE TASK WAS NOT SUSPENDED, RESUMING IT IS AN ERROR.
THIS GETS REFLECTED IN THE EVENT VARIABLE EV. EV NONZERO MEANS
RESUME PROCESSING IS COMPLETE.

	REQUEST

	REQUEST	#NAM,#PRI,#EV

ASSEMBLY:

	MOV	#EV,-(SP)	;EV TO TELL WHEN TASK HAS BEEN REQUESTED
	MOV	#PR,-(SP)	;PRIORITY. (UNUSED)
	MOV	#NAM,-(SP)	;NAM HAS TASK'S RAD50 NAME.
	TRAP	5

ACTION:

	THE TASK NAM IS STARTED. IF TASK NAM IS NOT IN STATE 0
(EXITED), THIS IS AN ERROR.
	NOTE THAT FOR REQUEST AND RESUME THE ACTUAL RAD50 TASK NAME IS
PUSHED ONTO THE STACK. FOR RESUME THE RA IS LITERAL ALSO.
	IF A NUMBER IS PUSHED ONTO THE STACK AS TASK NUMBER FOR RESUME
OR REQUEST, THE NUMBER (0,1,2,3,4,...) WILL BE TREATED AS THE NUMBER
OF THE TASK (ITS PRIORITY...) FROM THE START OF THE STL. THAT TASK
WILL THEN BE RESUMED OR REQUESTED AND WILL REQUIRE SOMEWHAT LESS TIME
FOR TASK LOOKUP THAN THE NAME METHOD. THE TWO MAY BE INTERCHANGED.

	EXIT

	EXIT	#EV	;EXIT. EV MAY BE REPLACED WITH 0 IF NOT NEEDED.

ASSEMBLY:

	MOV	#EV,-(SP)
	TRAP	6

ACTION:

	TASK BECOMES INACTIVE. IT MUST BE REQUESTED AGAIN TO RESTART.
EV IS SET NONZERO WHEN TASK HAS EXITED.

	DECLARE

	DECLARE	;TELL MSX SOMETHING HAS HAPPENED SO IT SHOULD SCAN TASKS.

ASSEMBLY:

	TRAP	7

ACTION:

	THIS MAKES MSX SCAN TASK TABLES TO SEE IF CONTROL SHOULD BE
SWITCHED TO ANOTHER TASK. IF IT SHOULD, IT THEN WILL. SIMPLY SETTING
AN EV NONZERO WILL NOT AUTOMATICALLY START ANOTHER TASK; THIS IS
A WAY TO DO SO, WHILE INTERRUPTS ARE ANOTHER.

	QTRAN

	QTRAN	#DEV,#QBLOCK,#EV	;DO I/O VIA QTRAN

ASSEMBLY:

	MOV	#EV,-(SP)
	MOV	#QBLOCK,-(SP)	;DOS-STYLE TRAN BLOCK
	MOV	#DEV,-(SP)	;WORD CONTAINING MSX LOGICAL UNIT/SUBUNIT #
				;OF DEVICE. UNIT # IN LOW BYTE; SUBUNIT IN HIGH
				;BYTE
	TRAP	10

ACTION:
	THIS REQUESTS SOME I/O BE DONE. EV IS NONZERO ON COMPLETION.
EV POSITIVE IMPLIES SUCCESS; NEGATIVE IMPLIES ERROR IN I/O.
	NOTE THAT THE WORD AHEAD OF A QTRAN EV IS THE TASK TO REQUEST
ON I/O COMPLETION. BE SURE IT IS 0 IF NONE SHOULD BE CALLED.

	MSX UNIT NUMBERS MAY REPLACE RAD50 DEVICE NAMES AS FOLLOWS:

DEV		LUN
KB INPUT	1
KB OUTPUT	2
DF		3	(NOT SUPPORTED UNDER STD-ALONE)
MT		4	(NOT SUPPORTED UNDER STD-ALONE)
CR		5	(NOT SUPPORTED UNDER STD-ALONE)
LP		6
DT		7
DK		8	(NOT SUPPORTED UNDER STD-ALONE)
VT		9	(NOT SUPPORTED UNDER STD-ALONE)

	UNDER RSX, THERE ARE A FEW MODS TO QTRAN.
QTRAN WILL STILL QUEUE UP I/O REQUESTS ON A PER-LUN BASIS
AVOIDING THE IMPLIED SUSPENSION RSX IMPOSES WHEN 2 QIO$
REQUESTS ARE OUTSTANDING. HOWEVER, THE QBLOCK IS JUST
THE QIO$ DIRECTIVE PARAMETER BLOCK (DPB), THE EV IS
THE I/O STATUS BLOCK (SO 2 WORDS MUST BE RESERVED THOUGH
ONLY THE FIRST IS TREATED AS AN EVENT VARIABLE BY MSX0), AND
THE DEV ARGUMENT IS SIMPLY THE RSX LUN. IF A LUN IS IN THE
RANGE PERMITTING QUEUING (ASSEMBLY PARAMETER), THE
REQUESTS WILL BE QUEUED. IF EV AND/OR LUN ARGUMENTS ARE
OMITTED, THEY WILL BE IGNORED AND THE DPB USED AS IS.
THEY WILL BE FILLED IN FOR QIO$ ONLY. ANY OTHER RSX
REQUEST MAY BE PASSED VIA QTRAN, BUT WILL JUST BE
EXECUTED IMMEDIATELY.

	THE WORD PRIOR TO THE I/O STATUS BLOCK MAY CONTAIN A
TASK NUMBER TO RUN ON I/O COMPLETION IN THE RSX VERSION. IF IT
CONTAINS A NUMBER EITHER 0 OR TOO LARGE NOTHING WILL HAPPEN. IF
THE NUMBER IS IN A LEGAL RANGE, THE NUMBERED TASK WILL BE
EXECUTED ON I/O DONE.
	************************************
		NOTE!!!!!!!!
	***********************************
	THIS REQUIRES THAT 3 WORDS BE RESERVED FOR THE I/O STATUS
	WORD, WITH ONE BEFORE AND ONE AFTER THE LABEL!!

	FOR SPEED, THE RSX VERSION ALLOWS TRAP CALLS TO
MSX0 TO BE REPLACED BY A JSR PC SEQUENCE.
	TO REPLACE THE SEQUENCE

	TRAP N

	USE THE SEQUENCE

	JSR	PC,MX.SVC
	.WORD	N

	(AN ADDITIONAL ENTRY POINT, MX.SV2, MAY BE USED IF
	THE TRAP CODE IS DOUBLED.)
	THIS SAVES CONSIDERABLE TIME FOR RSX USE; THE
RSX TRAP SERVICE OVERHEAD IS AVOIDED.
	RSX USERS SHOULD BE AWARE THAT FOR MSX0, THE EVENT
VARIABLE IS A WORD, NOT A BIT!!




	MSX SCANS IN 2 MODES. FULL-SCAN LOOKS AT ALL TASKS.
PART-SCAN LOOKS FROM THE CURRENT TASK'S POSITION DOWN THE
TABLE, DONE WHEN THER IS NO LOGICAL REASON TO SUSPECT
A TASK OF HIGHER PRIORITY COULD HAVE BECOME ACTIVE
BY A MSX DIRECTIVE. ALL DIRECTIVES EXCEPT SUSPEND, WAIT, AND
ORWAIT PERFORM FULL-SCANS.


	IN QTRAN I/O, THE QBLOCK IS SET UP EXACTLY AS A DOS TRAN
BLOCK FOR READ/WRITE. FOR SPECIAL FUNCTIONS, IF BOTH THE 1 AND 2
BITS OF THE TRAN BLOCK STATUS WORD ARE 1, IT IS ASSUMED A SPECIAL
FUNCTION IS WANTED. IN THAT CASE, THE MEMORY ADDRESS SLOT IN THE
TRAN BLOCK IS CONSIDERED A POINTER TO A DOS-STYLE SPEC BLOCK.
FOR THESE CALLS THE EV WILL CONTAIN THE SPEC BLOCK ADDRESS WHEN
THE OPERATION IS DONE.

	THE FORMAT OF THE TRAN BLOCK IS:

QBLOCK:	.WORD	0	;DEVICE BLOCK NUMBER
	.WORD	MEMADD	;MEMORY START ADDR
	.WORD	PWC	;POSITIVE WORD COUNT (BYTE COUNT EXCEPT UNDER DOS)
	.WORD	FUNC	;BIT 2=WRITE; BIT 4=READ; NEITHER=.SPEC CALL
	.WORD	0	;SPARE

	THE FUNC WORD IS SIMPLY PASSED TO THE DRIVER (AS ARE THE
OTHERS) AND THE CONTENT OF A QBLOCK FOR A GIVEN DEVICE IS
DEPENDENT ON THE DRIVER. THE WORD COUNT IS NEGATED BEFORE PASSING
TO THE DRIVER, BUT THE OTHER ARGUMENTS ARE LEFT ALONE. THE UNIT
NUMBER IS SENT TO THE DRIVER IN THE HIGH BYTE OF THE FUNC WORD
AND THE LOW BYTE OF FUNC IS SENT INTACT. THE DRIVER (IN THE STANDALONE
MSX) HAS ACCESS TO THE TCB ADDRESS OF THE TASK (AT ITS DDB+20) WHEN
EXECUTING. THE FORMAT OF A DDB IS INCLUDED IN THE CODE IN MXTRPS. THE UNIT
NUMBER MAY BE USED AS AN EXTENDED BLOCK NUMBER FOR AN APPROPRIATE
DEVICE.
	SUBUNITS ARE CONTROLLED BY THE UNIT SPECIFIER IN THE DEV
NUMBER IN THE CALL. MSX CANNOT HANDLE RAD50 DEVICE NAMES ACTUALLY
BUT WANTS ITS LOGICAL UNIT NUMBER IN THE LOW BYTE AND THE SUBUNIT
(DT0:,DT1:, DT2:, ETC. 0,1,OR 2, FOR EXAMPLE) IN THE HIGH BYTE.
	IF A .SPEC CALL IS ISSUED, THE FUNCTION IS GIVEN IN THE DEVICE
BLOCK NUMBER SLOT. LP: OPEN AND CLOSE FOR INSTANCE WOULD BE THE OFFSETS
FROM DRIVER START TO THE BYTE IN THE DRIVER CONTROL TABLE FOR THOSE
FUNCTIONS. DRIVERS DETERMINE THESE FUNCTIONS.

	INTERRUPTS

	WHEN AN INTERRUPT OCCURS, MSX MUST BE NOTIFIED SO IT
CAN MAINTAIN STACK USE CORRECTLY. IT USES 1 COMMON STACK FOR ALL
INTERRUPT PROCESSING AND MUST KNOW WHEN THAT STACK IS TO
BE ENTERED. A STANDARD POSTING PROCEDURE IS DONE IN MX.PST.

	THE CALL SEQUENCE IS

	JSR	R5,MX.PST	;WITH ONLY INTERRUPT PS,PC ON STACK
	.BYTE	PRI,RFLG

	PRI IS THE PRIORITY TO BE USED  IN PS FOR THE REST OF THE
INTERRUPT SERVICE ROUTINE AND MUST BE THE ACTUAL BYTE TO GO INTO
THE PS. THE INTERRUPT VECTORS SHOULD ALWAYS HAVE PRIORITY 7 
NEW-PS VECTORS AND USE THIS ROUTINE TO LOWER THE PRIORITY IF DESIRED.
	THE RFLG BYTE TELLS WHETHER TO SAVE REGISTERS (R5-R0) IF
NONZERO, OR NOT. RFLG=0 IMPLIES DO NOT SAVE REGS; RFLG=
NOT-0 IMPLIES SAVE REGS. REGS ARE SAVED ON THE COMMON (INTERRUPT)
STACK.
	ALL INTERRUPT ROUTINES SHOULD END IN RTI AFTER RESTORING ANY
REGISTERS. THE ROUTINE MUST RESTORE REGS ITSELF USING EITHER
THE MSX OR DOS REGISTER-RESTORE ROUTINES.

	TASKS CAN PREVENT TASK SCANNING BY SETTING THE LOW BYTE
OF MX.LOK NONZERO (SYSTEM USES HIGH BYTE) (ZERO?) WHICH WILL LET
INTERRUPTS OCCUR BUT KEEP CONTROL IN A TASK, POSSIBLY FOR 
CRITICAL TABLE MANIPULATIONS.
	USERS MUST UNLOCK THE SYSTEM TOO WHEN DONE. (ONE MAY HAVE
TO ISSUE A DECLARE TO ENSURE NOTHING IMPORTANT HAS BEEN MISSED TOO.)




	STAND-ALONE MSX0

	THERE IS A VARIANT OF MSX0 THAT WORKS IN A MEMORY-MAPPED
STANDALONE ENVIRONMENT. TASKS RUN IN USER SPACE, NORMALLY IN APR 0
UP, AND MSX0 AND HANDLERS RUN IN KERNEL SPACE. IN THIS VERSION
OF MSX, DEVICES ARE CONTROLLED BY HANDLERS THAT WORK AS EXECUTIVE
PROCESSES, AND THE TASK STATUS IS ALL SAVED IN THE SYSTEM TASK
LIST.
	THE STL ENTRIES ARE 24 WORDS LONGER FOR STANDALONE MSX
THAN FOR THE NORMAL RSX/DOS VERSIONS, AND THE EXTRA 24 WORDS OF
EACH ENTRY ARE LOCATED AFTER THE ONES DESCRIBED ABOVE. THEIR
CONTENT IS AS FOLLOWS:

	TASK R0
	TASK R1
	TASK R2
	TASK R3
	TASK R4
	TASK R5
	TASK APR 0
	TASK APR 1
	TASK APR 2
	TASK APR 3
	TASK APR 4
	TASK APR 5
	TASK APR 6
	TASK APR 7
	TASK PC
	TASK PSW
	THE MAPPING HERE IS ADEQUATE FOR 22-BIT SUPPORT PROVIDED
MX.BGN IS MODIFIED TO TURN IT ON. HOWEVER, NPR DRIVERS (AT PRESENT,
ONLY DT:) NEED TO BE MODIFIED TO HANDLE THE UMR MAPPING TO WORK IN
THIS MODE.
	ADDITIONAL WORDS ARE USED TO SUPPORT THE MULTIPLE-CPU
STRUCTURES OF THE MSX SYSTEM.
	WHEN A TASK IS STARTED, ITS START ADDRESS IS COPIED OVER
THE PC AND ITS "START APR1" WORD IS COPIED OVER APR 0. THE NORMAL
STATUS RESTORE IS THEN USED TO BRING THE TASK UP. THE MSX STL IS
EXPECTED TO HAVE ANY APR OR REGISTER CONTENTS SET UP INITIALLY
AS NEEDED, BUT THEREAFTER THE STL ENTRY WILL HAVE ALL THIS
INFORMATION COPIED INTO IT FROM THE TASK WHENEVER THE TASK IS
INTERRUPTED BY ANOTHER (OR BY A DIRECTIVE). THIS MEANS THAT
THE CONTENTS OF APRS 1 THROUGH 7 AND REGISTERS WILL TEND TO
PROPAGATE ACROSS CALLS, BUT THIS DIFFERS FROM THE RSX VERSION AND
SHOULD NOT BE COUNTED UPON. WHENEVER MSX STARTS A TASK, IT WILL
SET THE PREVIOUS MODE TO KERNEL AND THE CURRENT MODE TO USER
IN THE TASK'S PSW, TO ALLOW TASKS TO ACCESS KERNEL SPACE IF
THEY WISH TO DO SO (E.G. TO SET MX.LOK OR TO FLAG A SIGNIFICANT
EVENT.)

	IN THE STANDALONE MSX, ONE CANNOT USE A JSR PC SEQUENCE TO
ENTER AN EXECUTIVE ROUTINE. THE TRAP SEQUENCES QUOTED ABOVE WILL
HAVE THE DESIRED FUNCTIONS HOWEVER.
	TO PERMIT I/O TO BE DONE (AFTER A FASHION) FROM KERNEL
PROCESSES, THERE IS A SUBROUTINE, KNLQIO, THAT WILL ISSUE A
QTRAN AND A WAIT. IT IS CALLED VIA JSR PC WITH R1 POINTING
TO THE EVENT VARIABLE, R2 POINTING TO THE (DOS-STYLE) QTRAN
BLOCK, AND R3 CONTAINING THE LUN NUMBER FOR THE OPERATION.
CONTROL WILL RETURN AFTER DONE; THE ACTIVE TASK (IF ANY) IN USER
SPACE WILL BE DISABLED FROM EXECUTION UNTIL THE I/O COMPLETES.
	THIS IS BASICALLY TO ALLOW DDT TO PATCH USING THE AVAILABLE
I/O FACILITIES, OR TO DO DEVICE-INDEPENDENT THINGS.

	FOR A BIT OF EXTRA SPEED, THE STANDALONE VERSION OF MSX SOMETIMES
MAY BE SET TO USE THE EMT INSTRUCTION FOR TASK REQUESTS OR EXITS WITH NO
ARGUMENTS, AS AN ALTERNATIVE TO THE TRAPS ALREADY NOTED.
	EMT NNN		WILL REQUEST TASK NUMBER NNN (LEGAL
			WHERE NNN IS 177 OCTAL OR LESS, AND WHERE
			NNN IS A VALID TASK NUMBER).
				IF THE C BIT IS SET AT THE TIME
			THE EMT IS ISSUED, THE REQUEST WILL BE
			EFFECTIVELY A QRUN, WITH NO PRIORITY
			ARBITRATION PERFORMED. IF THE C BIT IS
			CLEAR, MSX WILL ENSURE THAT TASK NNN IS
			REALLY THE HIGHEST PRIORITY ELIGIBLE TASK
			BEFORE STARTING IT (EFFECTIVELY A PRIREQ).

	EMT NNN		WHERE NNN IS HIGHER THAN THE MAXIMUM VALID
			TASK NUMBER (OR NEGATIVE), WILL ACT AS AN
			EXIT DIRECTIVE.

	STANDALONE MSX USES THE DOS FORMAT TRAN BLOCKS FOR ITS
QTRAN DIRECTIVE. HOWEVER, THE EVENT VARIABLE IS REALLY A BLOCK OF
AT LEAST 2 WORDS. THE LABEL IS ON THE SECOND, AND THE FIRST GIVES
THE TASK NUMBER TO REQUEST WHEN THE I/O COMPLETES. IF THIS TASK
NUMBER IS NONZERO AND WITHIN THE VALID RANGE FOR THE SYSTEM,
THAT TASK WILL BE REQUESTED BY AN EFFECTIVE QRUN (NO PRIORITY
ARBITRATION) WHEN THE COMPLETION INTERRUPT IS SERVICED.

	THE MX.PST ROUTINE ACTS SOMEWHAT DIFFERENTLY IN STANDALONE MSX THAN
IN THE RSX VERSION. IN THE STANDALONE VERSION, INTERRUPTS WHEN POSTED WILL
MODIFY THE STACK ONLY WHEN THE SCANNER IS INTERRUPTED. IF A TASK IS
INTERRUPTED NO ACTION IS TAKEN, BUT COMPLETION RETURNS JUMP TO MX.RTI
TO SEE IF A SWITCH IS NEEDED DIRECTLY. THIS IS DONE IN MXIOHT, WHICH IS
PART OF THE I/O SYSTEM FOR STANDALONE MSX. IN THE STANDALONE VERSION,
I/O IS DONE AS PROCESSES RATHER THAN TASKS, AND ACTIVATIONS OF I/O
HANDLER TASKS ARE NOT NEEDED. ONLY COMPLETION RETURNS (WHICH ARE
SIGNIFICANT EVENTS) REQUIRE CONTEXT SWITCHES.
	FOR USER INTERRUPTS WISHING TO ALLOW CONTEXT SWITCHING, THE
CORRECT SEQUENCE IS TO SAVE THE CURRENT TASK STATUS AT INTERRUPT LEVEL
AND THEN CALL THE SCANNER:

	;(PROCESS INTERRUPT)	;(MUST SAVE/RESTORE ANY REGS USED)
	JSR	PC,U.RSAV	;SAVE CURRENT TASK CONTEXT. TOP OF STACK
				;MUST BE ONLY THE INTERRUPT. THIS MAY
				;BE BEFORE OR AFTER MX.PST IS CALLED,
				;AND ALL REGISTERS ARE FREE ONCE DONE
	JMP	MX.RTI		;GO OFF SCANNING OR DO RTI IF MX.SEV NOT SET.

	NOTE THAT AT THE U.RSAV CALL THE ONLY THING ALLOWED ON THE
TOP OF THE STACK IS THE PC,PS PAIR FROM THE INTERRUPT. U.RSAV WILL
ITSELF CHECK THAT A TASK WAS THERE AND RETURN IMMEDIATELY IF NOT.
	THE CALL JSR PC,U.RRES WILL GET BACK A TASK CONTEXT IF
ONE WAS THERE; THE C BIT WILL BE SET IF THE TASK WAS EXITED (USED WHEN
STARTING NEW TASKS). THE USER MODE SP AND ALL APRS AND REGISTERS WILL
BE SET UP. HOWEVER PLEASE NOTE: MSX MAKES NO VALIDITY CHECKS OF
ANY REGISTERS OR APRS, INCLUDING SP AND PC.

	THERE IS A COMMAND WHICH MAY BE ASSEMBLED INTO DDT TO ALLOW
ALL REGISTERS AND STATUS TO BE LOADED FROM A TCB; IT IS
	ADDRESS$UA

	IN THIS CASE, IF "ADDRESS" IS THE ADDRESS OF THE START (NAME
WORD) OF A TCB ENTRY, DDT WILL LOAD ALL ITS CONTEXT WITH THE SAVED
INFORMATION ABOUT A TASK IN THE FORMAT GIVEN ABOVE. THIS SHOULD
MAKE IT EASY TO DEBUG MULTITASK SYSTEMS IN THIS ENVIRONMENT.