DDT-11 - Dynamic Debugging Technique on the PDP-11

	DDT is a powerful debugging tool on the PDP11 that can
control execution of a program or display program or data in a
variety of formats. It can display or allow entry of data as
MACRO-11 instructions, octal or decimal constants, floating
point munbers, ASCII, RAD50, or, in some limited cases, hex
or other radices, or bytes of arbitrary length. It can single step
through programs, allow execution until breaks, or execute until
one or more memory locations changes. It allows users to define
symbols and displays addresses either absolutely or relative to
symbols. It can read symbol table files to automatically define
global symbols too, and caches these symbols internally to speed
searches.
	Where DDT is too big to fit into a task's context,
it may be assembled and linked to run in a separate task under
RSX11M, RSX11D, RSX11M+, or IAS and to debug another task
or a collection of tasks from a debug task, with all facilities
intact and available and only minor speed loss. This makes DDT
suitable for all PDP11 debugging chores.
	Under certain conditions, DDT may need to be sure tasks are
not shuffled too much, but it can operate in a mode ("pure send/
receive") that does not need any such constraint. It is able to
address a task directly, however, considerably faster than it
can pseudo-address the task by communicating with a "debug kernel",
and in this mode needs to be sure the task does not move until
a breakpoint is fully processed. These constraints apply only to
DDT debugging one task from another.
	It should be noted that DDT can operate using pure send
and receive data directives between tasks, and in this mode is
not sensitive to shuffling/checkpointing, etc. However, single
stepping with a watchpoint was measured about 3 times slower in
"pure send/receive" mode than in "DDT mapping" mode (50 instructions
per second vs. 16 instructions per second, single stepping and
examining 1 memory location per step; representative of the speed
of handling normal breakpoints, but worse than normal single
stepping.

Each  command in DDT/11  is identical to the  PDP-10 version whenever
possible.   In some cases,  DDT/10 commands have been  omitted in the
interest  of saving core and  making good sense.  The  following is a
list of the DDT/11 commands:
 n/	Open word n.  Type contents in current mode
  /	Open word pointed to by last typed value
 n<CR>	Modify currently open word to be n.  Close word.
 n<LF>	Modify, close, open next word
 n^	Modify, close, open previous word
 n<TAB>	Modify, close, open word pointed to by last typed address
 n\	Modify, close, examine word n
  \	Examine word pointed to by last typed value
n?	Type word n in RAD50 format (forces even address)
@	Types out location absolutely addressed by the open
	location (the same convention as <tab>, and the
	same as the DEC ODT convention for @ sign.
  $S	Change current mode to instruction type out ("Symbolic")
  $A	Addresses will be typed as absolute numbers ("Absolute")
  $R	Addresses will be typed relative to symbols ("Relative")
  $C	Change current mode to numeric type out	    ("Constant")
 $nR	Change current radix for $C to n (n read in decimal)
  $T	Change current mode to ASCII text output    ("Text")
 $5T	Change current mode to Radix-50 text output
 $nO	Change current mode to n bit byte typeout
  $H	Change to halfword (byte) mode (reset by $5T and $S)
	Note that the initial modes are $S and $8R.  These can be
	temporarily changed by the above commands and will return
	to the permanent setting by a carriage return.  The settings
	can be permanently changed by using two altmodes before the
	mode setting command ($$T sets permanent ASCII mode)
 n[	Open location n, type as a numeric
 n]	Open location n, type as instruction
 n!	Open location n, do not type value
  ;	Retype currently open word
  =	Retype currently open word as number
 n=	Type value of n as a number
  _	Retype currently open word as instruction
 $_	Retype currently open word symbolically
  i$X	Execute instruction i (cannot execute branches or jumps)
		Note the instruction executes in the context of the
	target task if multi-task DDT is in use.
  n$G	Start executing program at location n.  Default is to
	start executing at address in JOBSA (start of program)
  v$nB	Set breakpoint n at address v (n from 1 to 8 or can be omitted)
a,v$nB	Same as above but open address a at breakpoint
	If two altmodes are used, automatic proceding is enabled.  The
	breakpoint will cause the message to be typed and the program
	resumed.  If you type a character, the automatic proceding will stop.
  0$nB	Remove breakpoint n
   $B	Remove all breakpoints
   $P	Procede from breakpoint
  n$P	Procede from breakpoint n times (without halting)
	If two altmodes are used, the breakpoint will be proceded
	from automatically.
  n$UW	Set offset limit to n (used when typing addresses)
   $1UT	Turn on single stepping (break at each instruction)
  a$1UT	Turn on single stepping and open location a at each break
	If two altmodes are used, the single stepping will be
	done automatically.
   $UT	Turn off single stepping
  a:	Make current location have symbolic name a
v<a:	Make symbolic name a have value v
  a$$K	Delete symbolic name a
  a$K	Delete symbolic name a from typeout only
   $D	Perform an $K on the last symbol coloned (:)
l<u$$Z	Zero memory from l to u ;Location D.FILV Contains number filled in
  n$M	Set mask for searches (below) to n
l<u>s$W	Search core from l to u for word s.
l<u>s$E	Search core from l to u for effective address s.
l<u>s$N	Search core from l to u for word not equal to s.
addr$UInumber	Insert 32-bit floating-point number at addr
addr$UJnumber	Insert 64-bit floating point number at addr
addr$UX	EXamine floating point number at addr. Assumed to have
	precision in D.PRCN (2 or 4 for 32 or 64 bits) which is
	left over from last $UI or $UJ or set from console.
	Note that floating AC's are saved/restored only if FPCTL is
	set nonzero. If so, FPSTAT is FPU status and AC0-AC% are floating
	AC's.
addr$J	Display contents of (addr, addr+2) as a 32 bit integer in current
	radix.
addr$1Jnumber	Insert number at addr and addr+2 as a 32 bit integer.
	number is delimited by any character not legal in the current
	radix. The 32 bit integers are assumed stored as (low order,
	high order) in memory (addr=l.o., addr+2=h.o.).
addr$2Jnumber	Insert number (in current radix) at addr as a 16 bit number.
	This is provided in addition to the usual DDT methods since the
	DDT parser cannot handle bases higher than 10. Thus, this
	command gives a means to enter, as well as display, numbers in
	higher bases, such as hex.
$L	Close open core image file. Must be done prior to exit from DDT.
$1L	Prompt for and open core image file to use instead of virtual
	memory in $UM mode. CD.BLK is (lo,hi) base block number in file
	(initially 1,0) and CD.BAS is lowest address in file. DDT converts
	addresses to file relative form and reads or writes. If the
	/RO switch is used, the file is read only, else read/write, and
	it must be on SY:. If the /AB switch is used, DDT tries to do
	read/write logical block on a device directly.
$UO	Prompt for name of symbol table file. If a file is specified and
	exists, set to use it to resolve symbols. If file spec is null
	or does not exist, close existing symbol table file.
	$1UO will close any open symbol table file too but will erase
	DDT's internal "cache" of symbols. $UQ leaves that cache intact.
$UQ	Close symbol table file if any is open.
$UM	Turn on use of virtual map. Variables PAR0 through PAR7 will be used
	as APR's for all number entry or displays in any format.
$UU	Turn on virtual mapping and copy current User APR's into maps
	used by DDT. All addressing will be done via those virtual
	APR's.
$UK	Turn on virtual mapping and copy current Kernel APR's into
	maps used by DDT. All mapping will be done via these APR's.
	Note that if Kernel I and D space exists, $UK gets kernel D
	APRs and 1$UK gets I space kernel APRs.
$UV	Use standard DDT virtual mapping (no pseudo maps). This differs from
	the other commands in that no APR's are used; the others use the
	APR's that DDT is intialized with, which may be inadequate if the
	task is checkpointed and moved. DDT initializes in this mode and
	can, in it, access whatever a normal DDT can access (and conversely).
brk#<addr$UZ set memory break at addr. If brk# is higher than 8, clears
	out memory break. Done with single step mode and infinite
	proceed...slow. Note MEMCTL may be set 0 to turn off too.
	If MEMCTL is nonzero, the default proceed count is made
	infinite for single step, to allow these "watchpoints" to
	work without excess user effort. Note further that the
	watchpoint may be cleared EITHER by setting the address to
	0 OR by a $UZ command with brk# out of range (10 or over
	octal as normally assembled. A negative number will be
	out of range too.) The method of setting the memory address
	to 0 clears the one watchpoint but leaves the rest; using
	an illegal brk# will clear ALL watchpoints out.
brk#<0$UZ Turn off memory watchpoint numbered brk#, leaving others on.
11<0$UZ Turn off all memory watchpoints. Does not automatically
	leave single step mode however. Any number from 10 up, or
	a negative number, will suffice to turn off watchpoints.
	This effect can be obtained by putting 0 in the MEMCTL
	variable in DDT also. This form clears all old watchpoint
	addresses; zeroing MEMCTL will leave them intact for
	later use if desired.
  ; The following are controls for DDT macros, that is, sets of
  ; DDT commands stored and executed by the single $UC command.
$UE	Turn on echoing of macros. Macros are stored in DDT space
	at address D.KBBF as ASCII text using the standard DDT
	text storage syntax, up to 80 characters. Macros should
	end with negative bytes of data or the $US command to return
	to standard input, though they should eventually return
	with possible junk commands if this is omitted.
$UN	No echo of macros at the console.
$UC	Use core for input. Enables macros at D.KBBF to be read and
	executed as though they came from the console.
$US	Use Standard input device (console) for command input.
$UF<delim>text<delim> Fill in text of macro (up to 80 char) with any
	characters. Text is always read from console and the command
	terminates, filling in a legal end sentinel, after buffer
	full or recognition of the second delimiter character, which may
	be any ASCII character not in the text string.

	These macros are enabled by the D.MCRO assembly conditional
	defined.

		NOTE
	DDT mapping does not affect program execution; only displays
	are affected. Modifications to memory will use the current
	APR's, but breakpoints will not be put into arbitrary memory
	locations.
		The $UM, $UV, $UU and $UK commands only exist where the
	assembly conditional $VMEM was defined and DDT is linked to
	a common in the I/O page at APR 7.
; The following command is used to point DDT at a task in the system.
 ; It is automatically used in cases where DDT is debugging another
 ; task.
$UL<delim>TSKNAM<delim>  Read a task name (6 characters maximum) from
	the console (or macro) and locate its header and mapping
	information inside RSX11M. Then compute the APR mappings for
	that task and move them into the locations used by DDT for
	its pseudo mapping. This option requires that R$XMDB be defined
	and that DDT be assembled with $VMEM defined and with the
	appropriate RSX macros (normally [1,1]EXEMC) available for
	header, TCB, and window block offset definitions. Also, the
	task using such a version of DDT must have access to the I/O
	page via APR 7. This option only makes sense on fixed tasks
	or in systems without checkpointing, but may be useful in
	those systems for examining or modifying other tasks.
	The $UM command is needed to actually use the virtual APRs
	set up by the $UL command; $UL only sets them up for later
	use.

Note that numbers can be as any combination of the following:

	<Octal number>
	<Decimal number> .
	<Program symbol>
	" <Delimeter> <Two ASCII Characters> <Delimeter>
	"$ <Delimeter> <Three Radix-50 Characters> <Delimeter>
	<Instruction>

The operators +  (addition), - (subtraction), * (multiplication), and
' (division) are evaluated  from left to right unless parenthesis are
included.  The space is treated like a plus except after instructions
when  it is merely a  separator.   All input is  accepted in lower or
upper case and is folded (except for text.)

In addition to program symbols, the following are also defined for you:

 R0-R5	are the user registers.  R1/ would open register 1.
 SP	is the user's stack pointer
 PC	is the user's program counter
 $I	is the user status
 $2I	is the status of DDT
 $M	is the mask for searches
 $Q	is the value at the current address
 $V	is the value at the current address with the bytes switched
 $nB	is the address of breakpoint n
 JOBSA	is the starting address of your program.
In multi-task DDT, U.PSW and U.DSW are the target task's PSW and $DSW
	respectively. Then D.R0 thru D.PC are the DDT registers.
AC0-AC5 are the FPU registers where $D$FPU was defined at assembly
	(Note however that instructions still print the symbols R0
	through R5 instead of AC0-AC5.)
FPSTAT  is the FPU status register
FPCTL   controls FP save/restore. If 0, no save/restore of
        floating registers occurs. if nonzero, all FPU status is
        saved across calls. Initially the value of $D$FPU at assembly.
FPFMT   2 bytes for number decimals and width fo FP print field
D.PRCN  is the precision of FP print conversions. It may be 2 or 4
        for single precision or double precision outputs.
RSXEXT IS RSX-11-M or -D EXIT$S call
$$DOS is DOS-11 EXIT call
DDTODD is DDT odd addr SST table entry (RSX DDT only)
DDTIOT is DDT IOT table entry
DDTTRP is TRAP entry
DDTRES is RESERVED INST entry
DDTEMT is non-RSX EMT entry
D.FILV is number filled in by $Z command (initially 0)
(TASK NAME) is start address of task
BYE is equivalent to RSXEXT in RSX DDT
DDTBGN is the start address of DDT itself
PAR0 Is the current virtual memory APR 0. (PDR is always 4K R/W)
PAR1	is the current virtual APR 1
PAR2	is current APR 2
PAR3	is current APR 3
PAR4	is current APR 4 (all these are in virtual ($UM) space
PAR5	is current APR 5
PAR6	is current APR 6
PAR7	is current APR 7 (must be I/O page for this to work)
MEMCTL  is the control for memory breakpoints. MEMADR and MBPVAL
	are addresses and last seen values for watchpoints which
	are used if MEMCTL is nonzero. Note D.CT should be -1
	and DDT should be in single step mode to use memory
	watchpoints. The $UZ command establishes those
	conditions.
SR.CTL	if 0 allows normal DDT mapping to arbitrary memory areas,
	and if 1 allows send/receive data directives to be used
	for communication with a target task (if MU$DBG defined only!)
OVRBRK	If present, may contain 0 or the address of a special
	breakpoint. If nonzero, then if a breakpoint occurs from
	the address in OVRBRK, only the data from OVRBRK will
	be restored with the original instruction. It is expected
	that a break at $ALBP2 will be used here (the autoload
	completion point) so breakpoints may be redefined after
	an overlay load.
PRFCTL	If 0, turns off profiler (default) or if nonzero turns
	profiler on. If the profiler is on, then execution will
	be histogrammed. The address of each breakpoint (typically
	a single step with many proceeds in the proceed count; -1
	is infinite proceed count) will be compared with PRFBAS
	and if above it will have PRFBAS subtracted from it. The
	offset will then be shifted RIGHT by PRFSHF bits, and the
	result converted into a word offset. The word of PRFHST
	so found will be incremented, provided the offset is
	within the bound of PRFSIZ. Breakpoint then proceeds
	normally. Note that watchpoints also enable single step
	mode and permit execution profiles to be done. Only
	addresses of instructions will be monitored in this way
	and the PRFHST array, internal to DDT, may be examined
	at any time with the normal DDT commands. Since the PC
	at break is always available, no intertask message overhead
	occurs with profiler above that of single step overhead.
D.BMSK and
D.BTST	Used to support conditional breakpoints, in the following
	sense: if the D.BMSK array word corresponding to breakpoint
	number is nonzero, it is ANDed with the word opened at
	the breakpoint and if the result is different from the
	corresponding word in the D.BTST array (both are word arrays
	generally 9 words long), the breakpoint will be ignored.
Up to 160. user symbols (as presently defined) may be entered.
  .	represents the current location.  Thus .$1B puts
	breakpoint 1 at the currently opened location.

When  your program is  executing, the following  unexpected traps may
occur.  NXM! is  caused when  your  program requests  a  non-existant
memory or does a word operation on an odd address.  ILG! is caused by
an  illegal instruction.  BPT! is  caused by an entry  to DDT that is
unexpected (i.e. executing the BPT instruction or setting the T-bit).
Also TRP! means a TRAP, EMT! means an EMT was seen, and a few others
indicate the type of trap. (SEG! means memory protect error.)


	To include DDT with your task, just include on the input side
  of the taskbuild. thus, whn your normal TKB would be
  TKB MYFILE,MYFILE=MYFILE
  make it look like this:
  TKB MYFILE,MYFILE=MYFILE,[1,1]DDT/DA
    DDT will gain control at startup. To start your program, type
  <ESC>G where you type the ESC key, not the 5 characters "<ESC>".
  To exit prematurely, type  BYE<ESC>G (again the ESC key).
  A type-in of control Z will also exit DDT.

  Note that DDT does not prompt with anything!
 Where DDT is built to do its own echo, it echoes ESC as $. If not built
this way, DDT may not look like it echoes everything on VT52 or VT100
terminals, but will still function correctly.

 Some instruction mnemonics in DDT are nonstandard to reduce
the size of the instruction database. The following are the
nonstandard mnemonics and their standard counterparts:
      Nonstd	Standard
	HLT	HALT
	WAT	WAIT
	RST	RESET
	MK	MARK
	FA	FADD
	FS	FSUB
	FM	FMUL
	FD	FDIV
	GD	MFPD
	PD	MTPD
	CC	CFCC
	F	SETF
	I	SETI
	D	SETD
	L	SETL
	LS	LDFPS
	SS	STFPS
	S	STST
	C	CLRF
	T	TSTF
	AB	ABSF
	NG	NEGF
	ML	MULF
	MD	MODF
	AD	ADDF
	LD	LDF
	SB	SUBF
	CM	CMPF
	ST	STF
	DV	DIVF
	SX	STEXP
	SI	STCFI
	SD	STCFD
	LX	LDEXP
	LI	LDCFI
	LF	LDCDF
 This completes the list of nonstandard DDT instruction mnemonics.

 DDT was derived from the original program of S. Rubin @CMU for stand-
alone GDP PDP11s, and extensively modified and extended by G. Everhart
for DEC environments, bugfixes, floating point, multi-task use, symbol
table reads, hex radix, watchpoints, kernel mode dual mode support,
macros, and a few other things. There is a comment in the original
that credits an old version of ODT as the starting point S. Rubin used;
I haven't been able to find any of that old ODT code!
			G. Everhart, 1/12/81