SCREEN HANDLING ROUTINES (SCREEN)
        CHAPTER 1


                                   RSX-11M
                          SUBROUTINE  SPECIFICATION


                      Screen Handling Routines (SCREEN)


                                   Contents

                       1.   Introduction

                       2.   Subroutine Structure

                       3.   General Calling Sequence

                       4.   Subroutines and Parameters



                                 Appendices 

                       A.   Subroutine Summary

                       B.   Error Returns

                       C.   Assembly and Task Building

                       D.   Future Improvements Planned

                       E.   An Alternative Method for SYSTIME VDUs.





        SCREEN HANDLING ROUTINES (SCREEN)                        PAGE 2
        CHAPTER 1


        1.     INTRODUCTION

               SCREEN represents a set of subroutines which  allow  the
               user  fully  to  utilise  the capabilities of his V.D.U.
               Not only does it incorporate the standard facilities  of
               cursor-positioning,  screen  clearing  and  so on (which
               most VDUs support) but also the special facilities  such
               as  double-height characters, second font and so on that
               are available on only  a  few  terminals  (such  as  the
               SYSTIME MK3).

               SCREEN provides an interface to  these  facilities  that
               is:


                 (i) Easy-to-Use  (No  need  to  remember   complicated
                     escape sequences).

                (ii) Terminal Independent (The same program source  may
                     be  used  for  different terminal types - the only
                     difference is in the task-building stage).

               (iii) Language Independent (The subroutines support  all
                     the  standard  languages  available  on  RSX-11M -
                     MACRO-11, FORTRAN, COBOL AND BASIC-PLUS-2).




        SCREEN HANDLING ROUTINES (SCREEN)                        PAGE 3
        CHAPTER 2


        2.     SUBROUTINE STRUCTURE

               In any task using them the SCREEN subroutines fall  into
               3 distinct categories (4 for COBOL) as follows:-

               2.1  Terminal Characteristics Table (xxxTBL)

               Each terminal type has  its  own  characteristics  table
               (see  AppendiX  C).   This  is  a  subroutine consisting
               purely of data defining the capabilities of the terminal
               and  how to use them in a format that can easily be read
               by the control subroutine.

               For each terminal type this module  also  defines  which
               subroutines   are   legal  by  defining  the  equivalent
               operator code (FD.XXX) or not.

               2.2  Control Subroutine (CTLOUT)

               This subroutine does all the real work.  It is called by
               the specific subroutines with the required operator code
               value in one of the registers.  It checks that the given
               code   is  valid  for  the  current  operator  type  and
               constructs the required control sequence in  the  output
               buffer  with  reference  to the Terminal Characteristics
               Table.  If so required  it  then  outputs  the  required
               characters on the given LUN (See Chapter 3).

               2.3  Specific Screen Subroutines (CURPOS, etc.)

               These  are  the  routines  which  translate  the  user's
               requirements   into   operator  codes  for  the  Control
               Subroutine.  There is one subroutine for each  facility,
               and  each  subroutine  merely sets the relevant operator
               code and calls the Control Subroutine to execute it.

               2.4  (COBOL only) Common Area Setup Routines

               The Control subroutine communicates with the  user  task
               by  means  of  a  COMMON  area  (.PSECT) which holds the
               relevant  information  (e.g.   Row  Number  and   Column
               Number  for  cursor  positioning).  Unfortunately, COBOL
               cannot currently map to such a COMMON area, so for COBOL
               tasks  the  information  has  to be set up in the COMMON
               region by means of specific subroutines (see Chapter 4).




        SCREEN HANDLING ROUTINES (SCREEN)                        PAGE 4
        CHAPTER 3


        3.     GENERAL CALLING SEQUENCE

               As indicated in Chapter 2, communication with the SCREEN
               subroutines  is  done  by  means of a COMMON area, which
               contains 9 words, as follows:-

               ADDBUF - Address of buffer to hold control characters.

               TOTBYT - Length of buffer to hold control characters (in
                        bytes).

               BYTCNT - Number of bytes in buffer currently used.

               COLNO  - Column Number for Cursor Positioning.

               ROWNO  - Line Number for Cursor Positioning.

               TABCNT - Tab Count for Tabbing.

               LINENO - Line Number for setting Scroll Base.

               OUT    - Flag to control whether the  Control Subroutine
                        outputs the sequence or not (1 = Yes).

               LUN    - Logical Unit Number for Output if OUT = 1.

               These are words rather than bytes because some languages
               do not support bytes.

               The common area definition, suitable for inclusion in  a
               user program, is given in the files.

                    SCREEN.MAC (for MACRO-11)
                    SCREEN.FTN (for FORTRAN)
                    SCREEN.B2S (FOR BASIC-PLUS-2)

               As  explained  before,  COBOL  does  not  support   this
               structure,  and the subroutines described in Chapter 4.2
               must be used.  However, a file is supplied defining  the
               variables needed in COBOL,

                    SCREEN.LIB

               Each of these files also contains  a  buffer  (40  bytes
               long)  suitable for use by the Screen Subroutines.  This
               may be changed by the user, but should not be less  than
               20  bytes  long  (which  will  cover  all single control
               sequences).

               Before any SCREEN routines can  be  called,  the  fields
               ADDBUF,  TOTBYT  and  BYTCNT must be initialised.  If we
               suppose that the user is using the default buffer  BUFF,
               then   to  set  up  ADDBUF  he  should  do  one  of  the



        SCREEN HANDLING ROUTINES (SCREEN)                        PAGE 5
        CHAPTER 3


               following:-

               MACRO        - MOV #BUFF,ADDBUF

               FORTRAN      - CALL GETADR (ADDBUF, BUFF)

               BASIC-PLUS-2 - CALL GETADR BY REF (ADDBUF%, BUFF$)

               COBOL        - CALL "SETBUF" USING BUFF,TOTBYT.
                              (See Chapter 4.2)

               TOTBYT and BYTCNT can  be  set  up  in  the  normal  way
               (except for COBOL).

               If the Control Subroutine is to do the output, then  OUT
               and  LUN  should also be set up.  The standard LUNs used
               by the languages are:-

               MACRO        - LUN 5 defaults to TI:

               FORTRAN      - The TYPE command uses LUN 5

               BASIC-PLUS-2 - The PRINT command uses LUN 13

               COBOL        - The DISPLAY command uses LUN 1.

               These defaults are set up for the first 3 languages, but
               for COBOL a

                    CALL "SETLUN"

               should be performed to set the default (although a  call
               to "SETBUF" also sets the default).

               In FORTRAN  or  MACRO-11  other  LUNs  can  be  used  if
               required just by altering the value of LUN, but the user
               is advised against using other LUNs for BASIC-PLUS-2  or
               COBOL where the LUN/device correlation is less obvious.

               The OUT flag should also be set  to  1  if  the  Control
               Subroutine  is to do the output.  For COBOL this is done
               by doing a

                    CALL "SETOUT"

               (although a call to "SETBUF" also sets OUT to 1)

               Usually for high-level languages it is  more  convenient
               for the output to be done by the Control Subroutine than
               by the task.

               Having set up the initial  conditions,  the  subroutines
               may now be invoked simply by



        SCREEN HANDLING ROUTINES (SCREEN)                        PAGE 6
        CHAPTER 3


                    CALL INVON    - MACRO, FORTRAN OR BASIC-PLUS-2

               or   CALL "INVON".  - COBOL

               The three subroutines  CURPOS,  SCRBAS  and  TAB  (q.v.)
               require   values   to   be   set   up   in   the  Common
               Area.  Variations of these exist as CURPS1,  SCRBS1  and
               TAB1 where the parameters are supplied in the subroutine
               call.  These are mainly for use in  COBOL  programs  but
               may  be  used  from  the  other  languages as well if so
               desired.

               In the specific  subroutine  descriptions  that  follow,
               each subroutine name is accompanied by its operator code
               descriptor (FD.XXX).  This  is  because  if  you  use  a
               subroutine such as

                    CLSCNR - Clear Screen(Rest)

               on a terminal which does not support the facility  (e.g.
               SYSTIME  MK2),  then  the  Task  Builder  will report an
               'undefined symbol' of

                    FD.CSR

               which is the corresponding operator code descriptor.

               Note that care must be  exercised  when  using  standard
               language  statements  to  output  text at a given cursor
               position,  as  the   statements   often   have   implied
               carriage-control.

               In MACRO-11 specify a  Carriage-Control  (3rd  param  in
               IO.WLB) of 0.

               In  FORTRAN  specify  both  '+'  and  $  in  the  FORMAT
               Statement (e.g.  ('+',$,'TEXT')).

               In COBOL ensure  that  there  was  a  DISPLAY...WITH  NO
               ADVANCING before the relevant output.

               In  BASIC-PLUS-2  append  a  semi-colon  to  the   PRINT
               statement (e.g.  PRINT A$;).

               Examples  of  the  language  are  given   in   TEST.MAC,
               TEST.B2S, TEST.FTN or TEST.CBL.




        SCREEN HANDLING ROUTINES (SCREEN)                        PAGE 7
        CHAPTER 4.


        4.     SUBROUTINES AND PARAMETERS

               4.1   General Subroutines

                 (i) RESET (FD.RST)

                     Resets the terminal to  its  initial  state  (i.e.
                     state after being switched on).

                (ii) TAB (FD.TAB)

                     Moves the cursor on the current line to the column
                     number specified in TABNO.
                     Columns are numbered starting at 1 (the  left-hand
                     margin).

                     The alternate entry point for this request is

                     TAB1 (TABNO)

                     where the tab number is  passed  as  a  parameter.
                     The second entry point must be used for COBOL.

               (iii) CURPOS (FD.POS)

                     Moves the cursor  to  the  position  specified  by
                     COLNO  and ROWNO for line number and column number
                     respectively.

                     Columns are  numbered  starting  from  1  for  the
                     left-hand margin.

                     Lines are numbered starting from 1 for the top  of
                     the screen.

                     -1 may be specified in either ROWNO  or  COLNO  to
                     represent  the  bottom  line  of the screen or the
                     right-hand column respectively.

                     If either value  is  outside  the  limits  of  the
                     device, the request is ignored.

                     The alternative entry point for this request is

                     CURPS1 (ROWNO,COLNO)

                     where the line and column numbers  are  passed  as
                     parameters.   The  second entry point must be used
                     for COBOL.

                (iv) NEWLIN (FD.NLN)

                     Advance the cursor to the beginning  of  the  next



        SCREEN HANDLING ROUTINES (SCREEN)                        PAGE 8
        CHAPTER 4.


                     line.

                 (v) BELL (FD.BEL)

                     Ring the bell on the terminal.

                (vi) DISCTL (FD.CTL)

                     Disable control characters on the  terminal.  This
                     means  that  keys depressed with the CTRL key also
                     depressed will be ignored.

               (vii) ENACTL (FD.DET)

                     Re-enable control characters.

              (viii) CLLINA (FD.CLA)

                     Clear the whole of the current line from column  1
                     to the end.

                (ix) CLLINR (FD.CLR)

                     Clear the  rest  of  the  current  line  from  the
                     current cursor position.

                 (x) CLSCNA (FD.CSA)

                     Clear the  whole  of  the  screen  from  the  home
                     position  (1,1)  to  the  end.   Note that on most
                     terminals the cursor is left at the Home position.

                (xi) CLSCNR (FD.CSR)

                     Clear the rest of  the  screen  from  the  current
                     cursor position to the end.

               (xii) HOME (FD.HOM)

                     Move the cursor  to  the  Home  position  (Line  1
                     Column 1).

              (xiii) INVON (FD.ION)

                     Set the screen into Inverse Video mode.  Note that
                     the   effect  of  this  varies  from  terminal  to
                     terminal.  On some terminals (e.g.   SYSTIME  MK3)
                     this  just  sets  an  Inverse  On flag so that all
                     characters displayed subsequently at the  terminal
                     are displayed in Inverse Video until the switch is
                     turned off.  On  other  terminals  (e.g.   SYSTIME
                     MK2)  this  results  in  an actual character being
                     output on the screen and all  characters  on  that



        SCREEN HANDLING ROUTINES (SCREEN)                        PAGE 9
        CHAPTER 4.


                     line  to  the  right  of it will appear in inverse
                     video (whether these already are displayed  later)
                     up  to  any  Inverse  off  character on that line.
                     Characters on other lines are not affected at all.

               (xiv) INVOFF (FD.IOF)

                     Switch off the Inverse Video mode.  See (xiii).

                (xv) LED1ON (FD.LT1)

                     Switch on the lst LED on the terminal.

               (xvi) LED2ON (FD.LT2)

                     Switch on the 2nd LED on the terminal.

              (xvii) LED3ON (FD.LT3)

                     Switch on the 3rd LED on the terminal.

             (xviii) LED4ON (FD.LT4)

                     Switch on the 4th LED on the terminal.

               (xix) LEDOFF (FD.LOF)

                     Switch off all the LEDs on the terminal.

                (xx) PAGMOD (FD.PON)

                     Set the terminal into Page Mode - i.e.  a CR/LF on
                     the  bottom  line  will position the cursor to the
                     Home Position without scrolling.

               (xxi) SCRMOD (FD.POF)

                     Set the terminal into Scroll Mode - i.e.  a  CR/LF
                     on  the  bottom  line will cause the whole page to
                     scroll up a line.

              (xxii) BLNKON (FD.BON)

                     Set the terminal into Blinking On Mode.

             (xxiii) BLNKOF (FD.BOF)

                     Set the terminal into Blinking Off Mode.

              (xxiv) UNDRON (FD.UON)

                     Set the terminal into Underscore On Mode.




        SCREEN HANDLING ROUTINES (SCREEN)                       PAGE 10
        CHAPTER 4.


               (xxv) UNDROF (FD.UOF)

                     Set the terminal into Underscore Off Mode.

              (xxvi) CURSR1 (FD.CT1)

                     Set the cursor to be a Static Block.

             (xxvii) CURSR2 (FD.CT2)

                     Set the cursor to be a Flashing Block.

            (xxviii) CURSR3 (FD.CT3)

                     Set the cursor to be a Static Underline.

              (xxix) CURSR4 (FD.CT4)

                     Set the cursor to be a Flashing Underline.

               (xxx) FONT1 (FD.FT1)

                     Set the terminal to use Character Font 1.

              (xxxi) FONT2 (FD.FT2)

                     Set the terminal to use Character Font 2.

             (xxxii) FULINT (FD.FUL)

                     Set the terminal into Full Intersity Characters.

            (xxxiii) HLFINT (FD.HLF)

                     Set the terminal into Half Intersity Characters.

             (xxxvi) PAGE 1 (FD.VP1)

                     Direct all future output to VDU Page 1.

              (xxxv) PAGE 2 (FD.VP2)

                     Direct all future output to VDU Page 2.

             (xxxvi) PRNTER (FD.PRT)

                     Direct all future output to the Slave Printer.

            (xxxvii) DMPSCR (FD.DMP)

                     Dump the contents of the  screen  onto  the  Slave
                     Printer.




        SCREEN HANDLING ROUTINES (SCREEN)                       PAGE 11
        CHAPTER 4.


           (xxxviii) DISP0 (FD.DP0)

                     Hide both VDU Pages.

             (xxxix) DISP1 (FD.DP1)

                     Display VDU Page 1 but Hide VDU Page 2.

              (xxxx) DISP2 (FD.DP2)

                     Hide VDU Page 1 but Display VDU Page 2.

             (xxxxi) DISP12 (FD.DP3)

                     Display both VDU Pages.

            (xxxxii) STRCUR (FD.STR)

                     Store the current cursor position.

           (xxxxiii) RSTCUR (FD.RES)

                     Restore the cursor to its stored position.

            (xxxxiv) SNGWID (FD.SWD)

                     Output characters as Single Width.

             (xxxxv) DUBWID (FD.DWD)

                     Output characters as Double Width.  Note that some
                     terminals  only allow Double Width characters that
                     are double Height as well.

            (xxxxvi) SNGHGT (FD.SHT)

                     Output Characters as Single Height.

           (xxxxvii) DUBHGT (FD.DHT)

                     Output Characters  as  Double  Height.  Note  that
                     some terminals only allow Double Height characters
                     that  are  Double  Width   as   well.  Also   some
                     terminals  regard the Double Height characteristic
                     as:

                       (a) Line Specific
                  or   (b) Divided into Double Height Upper and
                           Double Height Lower.

                     If  in  doubt  consult  your  terminal   Technical
                     Specification.




        SCREEN HANDLING ROUTINES (SCREEN)                       PAGE 12
        CHAPTER 4.


         (xxxxviii)  SCRBAS (FD.BAS)

                     Set the terminal's scroll base to the line defined
                     by LINENO.  If the line number is out of range for
                     the terminal the request is  ignored.   Note  that
                     various   terminals   implement  Scroll  Bases  in
                     different manners (the SYSTIME MK3, for  instance,
                     has 2 different specifiable Scroll Bases).

                     The alternative entry point for this request is

                       SCRBS1 (LINENO)

                     where the line number is passed  as  a  parameter.
                     The second entry point must be used for COBOL.


               4.2   COBOL - Specific Subroutines

                 (i) SETBUF (BUFF, TOTBYT)

                     This routine stores the address of the buffer BUFF
                     in  ADDBUF  in the COMMON area and the contents of
                     TOTBYT (which should be  the  length  of  BUFF  in
                     bytes) in TOTBYT in the COMMON area.

                     It also sets BYTCNT in the COMMON area to 0
                                  OUT     "  "     "     "   " 1
                                  LUN     "  "     "     "   " 1

                (ii) SETLUN (LUN)

                     This routine stores the contents  of  LUN  in  the
                     variable LUN in the COMMON area.  If the parameter
                     is omitted a value of 1 is assumed.

               (iii) SETOUT (OUT)

                     This routine stores the contents  of  OUT  in  the
                     variable  OUT  in  the  COMMON area.  If OUT is -1
                     then the current contents of the buffer are output
                     to the terminal and OUT is reset to 0.

                     If the parameter  is  omitted  a  value  of  1  is
                     assumed.

                (iv) GETCNT (BYTCNT)

                     This routine returns the current value  of  BYTCNT
                     in  the  COMMON area into the variable BYTCNT.  If
                     the parameter is omitted the request is ignored.



        SCREEN HANDLING ROUTINES (SCREEN)                       PAGE 13
        APPENDIX A


                                  APPENDICES

        A.     SUBROUTINE SUMMARY

               RESET     Reset terminal

               TAB       Move cursor to given column

               CURPOS    Position cursor at given line/column

               NEWLIN    Move cursor to start of next line

               BELL      Ring the terminal bell

               DISCTL    Disable control characters

               ENACTL    Enable control characters

               CLLINA    Clear the whole line

               CLLINR    Clear the rest of the line

               CLSCNA    Clear the whole screen

               CLSCNR    Clear the rest of the screen

               HOME      Move the cursor to HOME

               INVON     Switch Inverse Video On

               INVOFF       "      "      "   Off

               LED1ON    Switch LED1 On

               LED2ON       "    " 2  "

               LED3ON       "    " 3  "

               LED4ON       "    " 4  "

               LEDOFF       "   all LEDs off

               PAGMOD    Put terminal into Page Mode

               SCRMOD     "     "       "  Scroll Mode

               BLNKON    Set Blinking On

               BLNKOF     "     "     Off

               UNDRON     "  Underlining On

               UNDROF     "       "      Off



        SCREEN HANDLING ROUTINES (SCREEN)                       PAGE 14
        APPENDIX A


               CURSR1    Set cursor to Static Block

               CURSR2    Set cursor to Flashing Block

               CURSR3    Set cursor to Static Underline

               CURSR4    Set cursor to Flashing Underline

               FONT1     Set terminal into character Font 1

               FONT2      "     "       "      "       "  2

               FULINT    Set characters to be Full Intensity

               HLFINT     "       "      "  " Half Intensity

               PAGE 1    Direct Output to VDU Page 1

               PAGE 2       "     "     "  "   "   2

               PRNTER       "     "     " Slave Printer

               DMPSCR    Dump screen contents to Slave Printer

               DISP0     Hide both VDU Pages

               DISP1     Display VDU Page 1 only

               DISP2        "     "    "  2   "

               DISP12       "    both VDU Pages

               STRCUR    Save current cursor position

               RSTCUR    Restore saved cursor position

               SNGWID    Set characters to be Single Width

               DUBWID     "        "     "  " Double   "

               SNGHGT     "        "     "  " Single Height

               DUBHGT     "        "     "  " Double   "

               SCRBAS    Set Scroll Base

               SETBUF    Set Buffer address and length (COBOL only)

               SETLUN    Set Logical Unit Number (COBOL only)

               SETOUT    Set Output Flag (COBOL only)

               GETCNT    Get Current Byte Count (COBOL only)



        SCREEN HANDLING ROUTINES (SCREEN)                       PAGE 15
        APPENDIX A


        B      ERROR RETURNS

               Errors are returned in R0.  The possible values are:-

                         0 = Success
                         1 = Feature not Supported
                        -1 = Insufficient Room in Buffer

               As High-Level languages cannot usually  access  R0,  the
               value of BYTCNT is also negated if there is Insufficient
               Room in the Buffer.  If there  is  any  chance  of  this
               happening, it must be checked for.



        SCREEN HANDLING ROUTINES (SCREEN)                       PAGE 16
        APPENDIX C


        C.     ASSEMBLY AND TASK-BUILDING

               Each subroutine is merely assembled with a line  similar
               to
                      MAC CURPOS = CURPOS

               and included in the library SCREEN.OLB.  As  the  XXXTBL
               modules all contain the same global variables, they must
               be included in the library with the /-EP switch.

               To build a task using the subroutines, a line should  be
               used similar to

               TKB TEST  =  TEST,[1,1]SCREEN/LB:XXXTBL,SCREEN/LB,  (any
               language - specific libraries)

               where XXX defines the terminal type to be  used.   There
               are currently 8 terminal types, as follows:-

               (i)  L36

               Any hard-copy device (e.g.  LA36)
               Supports function (ii),(iii)[as CR/LF],(iv) and (v)

               (ii)  MK2

               The  SYSTIME  MK1  or   MK2   terminals   (or   MK3   in
               compatibility mode)
               Supports functions (i) - (v), (viii), (ix), (x), (xii) -
               (xxi).

               (iii)  MK3

               The SYSTIME MK3 terminal
               Supports all functions.

               (iv)  V52

               The VT52 terminal (or VT100 in compatibility mode)
               Supports functions (i) - (v), (viii) - (xii)

               (v)  V5H

               The VT50H terminal
               Supports functions (i) - (v), (viii) - (xii)

               (vi)  V50

               The VT50 terminal
               Supports functions (i), (ii), (iv), (v), (viii) - (xii)

               (vii)  VTC




        SCREEN HANDLING ROUTINES (SCREEN)                       PAGE 17
        APPENDIX C


               The VT100 terminal
               Supports functions (i) - (v), (viii) - (xiv)

               (viii)  H15

               The Hazeltine 1500 or 2000 terminals
               Supports functions (ii) - (v), (viii) - (xii)

               Note  that  as  explained  previously,  any  attempt  to
               reference  a  function  which  is  not  supported by the
               terminal type will produce undefined symbol error in the
               Task-Builder   for   the   corresponding  Operator  Code
               descriptor.  The program can  still  be  used,  but  the
               Control  Subroutine  will  just  ignore  the requests it
               cannot handle.



        SCREEN HANDLING ROUTINES (SCREEN)                       PAGE 18
        APPENDIX D


        D.     FUTURE IMPROVEMENTS PLANNED

               (i)   Extend VT52 and VT100 support.

              (ii)   Provide interface to Graphics capability of
                     terminals.

             (iii)   Handle RSX's insertion of CR/LF after
                     80 characters.



        SCREEN HANDLING ROUTINES (SCREEN)                       PAGE 19
        APPENDIX E


        E.     AN ALTERNATIVE METHOD FOR SYSTIME VDUs

               Programs wishing only to perform

               (i)  Cursor Positioning

              (ii)  Screen Erases

             (iii)  Line Erases

               on Systime terminals may use  an  alternative  approach.
               In  this  the user outputs the actual cursor positioning
               characters at the front of his display string.

               To do this the programmer  uses  a  combination  of  the
               following variables:-

               ATT     -  Prefix String for Cursor Positioning

               COL     -  80-element array defining the column to
                          be used

               LIN     -  24-element array defining the line to
                          be used

               ERASE   -  String to Home Cursor and Erase Whole
                          Screen

               NULL    -  String required to follow ERASE on
                          Systime MKI/II terminals

               ERALIN  -  String to Erase from current cursor
                          position to end of line

               (Note  that  in  BASIC-PLUS-2  each  variable  name   is
               suffixed with a $).

               The definitions of ATT,COL,LIN,ERASE and ERALIN are held
               in the files

                         CURSOR.MAC   (MACRO-11)
                         CURSOR.FTN   (FORTRAN)
                         CURSOR.B2S   (BASIC-PLUS-2)
                         CURSOR.LIB   (COBOL)

               If writing in FORTRAN  or  MACRO-11,note  that  ATT  and
               ERASE are 2 bytes long each, and ERALIN and each element
               of COL and LIN are one byte long.

               These variables are used as follows:-

                  (i)     To Position Cursor to Column 10 on Line 5
                          and output the text "HELLO" from a COBOL



        SCREEN HANDLING ROUTINES (SCREEN)                       PAGE 20
        APPENDIX E


                          Program:-

                          DISPLAY ATT,COL(10),LIN(5),"HELLO"

                 (ii)     To Clear the Screen from a FORTRAN program
                          (assumed on a MKII VDU):-

                          TYPE 100,ERASE,NULL
                          100 FORMAT (2A2)

                (iii)     To Position Cursor to Column 10 on Line 5,
                          output "FILENAME >" and Clear the rest
                          of the line, from a BASIC-PLUS-2 Program:-

                          PRINT ATT$;COL$(10%);LIN$(5%);'FILENAME >';
                             ERALIN$;

               and so on.

               The sample  programs  supplied  (TEST.MAC  etc.)  use  a
               mixture of the two methods for demonstration purposes.