INTRODUCTION

            As  the SYSTIME hardware is not identical to that supplied
            and supported by DEC, modifications have to be made to the
            standard  DEC  Operating  Systems  to  support them.  This
            document  describes  those  changes  as applied to RSX-11M
            V3.2  and  RSX-11M-PLUS  V1.0.    It is divided into three
            sections:-

                    Changes for the Storage Module Drives (SMDs)
                    Changes for the AMPEX Cartridge Drives
                    Changes for the SYSTIME MKII/MKIII terminals

            Each  section  describes  briefly  the  relevant  hardware
            differences and then the patches that are necessary.

            Hard  copies  of  all the patches are stored in the binder
            marked "SYSTIME Hardware Patches for RSX-11M/M-PLUS".




                                CHAPTER 1

                          Storage Module Drives

    a)      Hardware Differences.

            The  Storage  Module Drives are built to look like the DEC
            RP02/RP03   drives.    The  differences  (as  far  as  the
            operating  system  is  concerned)  lies  in  the number of
            Sectors  per  Track,  the number of Tracks per Surface and
            the  number of Surfaces per Drive.  The second of these is
            rarely  used  directly,  but instead the number of Sectors
            (Blocks)  per  Drive  (the  product of the above three) is
            usually  used.    For  DEC  and SYSTIME disks these values
            are:-

            Disk Type     Surfaces     Sectors      Blocks
                          per Drive    per Track    per Drive

            DEC RP02      20.          10.          40000.
            DEC RP03      20.          10.          80000.
            SYS 16MB      5.           32.          32000.
            SYS 32MB      5.           32.          64000.
            SYS 64MB      5.           32.          128000.
            SYS 128MB     19.          32.          243200.
            SYS 256MB     19.          32.          486000.

            To  distinguish between the RP02 and RP03 drives, there is
            a  special  bit  (the 'RP03 bit') set in one of the device
            registers  (the  Device Status Register).  This is used to
            distinguish either between 32MB and 64MB drives or between
            128MB  and  256MB drives.  Because of the way this is used
            by  SAV  (see  later)  RSX  systems  should really only be
            configured with:-

                    all 16MB drives, or
                    a mix of 32MB drives and 64MB drives, or
                    a mix of 128MB drives and 256MB drives

            plus, of course, any non-SMD drives.  This restriction can
            be overcome if necessary, but is not recommended.

            The  following  Software  Patches  are for the most common
            combination,  viz.  32MB  and  64MB  drives.   The changes
            necessary  for  the  other  drives should be obvious.  The
            patches   have   been   tested   for   both   RSX-11M  and
            RSX-11M-PLUS.    As  all SYSTIME systems are assumed to be
            running on SMDs and not on RP11s these patches are already
            incorporated into the files on the distribution disk.





    b)      RSX-11M

            Four files need to be changed for RSX-11M as follows:-

            1)      [11,10]DPDRV.MAC

            This  is  the  source file for the driver for the RP11/SMD
            drives  during  online  operation.   It converts a logical
            block  number to a cylinder/track/block address, and it is
            this calculation that must be changed:-

            After 10$: after DPINI change

                    DIV     #100.,R1
            to
                    DIV     #80.,R1
            and
                    DIV     #5,R1
            to
                    DIV     #32.,R1

            2)      [200,200]SGNPER.CMD

            This  is  the  file which creates the UCBs for the devices
            during  System Generation.  As the DP UCB contains a block
            count for the device this must be modified for SMDs:-

            After .DP30: change

                    .SETN TEMPN4 34200
            to
                    .SETN TEMPN4 172000

            and after .DP10: change

                    .SETN TEMPN4 116100
            to
                    .SETN TEMPN4 175000





            3)      [12,10]SPCDRV.MAC

            SAV and BOO do not use the standard system driver, but use
            a  special  driver  contained  in this file, which must be
            changed for SMDs as in 1:-

            After $DPDRV change

                    MOV     #10.,R4
            to
                    MOV     #32.,R4

            and after 30$: after $DPDRV: change

                    MOV     #20.,R4
            to
                    MOV     #5.,R4

            This  file  should  then  be assembled and replaced in the
            relevant library, like so:-

            SET /UIC=[1,24]
            MAC SPCDRV=[1,1]EXEMC/ML,[11,10]RSXMC/PA:1,[12,10]SPCDRV
            LBR SAV/RP/-EP=SPCDRV

            4)      [12,10]SAVSUB.MAC

            When  a  'Saved System Image' is booted, SAV sizes all the
            hardware  on the system before RSX-11M starts up.  For the
            RP11/SMD  controller  it  does  this  by setting a default
            number  of  blocks  and  then,  if  the 'RP03 bit' is set,
            doubling  that  number.  This value is then put in the UCB
            for  the  relevant  disk.   (Note that this means that for
            systems  using  16MB  drives  this file must be altered or
            else,  no  matter what was specified at System Generation,
            the   system   will   be   brought  up  with  32MB  drives
            configured.)

            After DEVSIZ: change

                    0,40000.
            to
                    0,175000

            This  file  should  then  be assembled and replaced in the
            relevant library, like so:-

            SET /UIC=[1,24]
            MAC SAVSUB=[1,1]EXEMC/ML,[11,10]RSXMC/PA:1,[12,10]SAVSUB
            LBR SAV/RP/-EP=SAVSUB





    c)      RSX-11M-PLUS

            The  changes  required  for  RSX-11M-PLUS  are  similar in
            effect  to  those for RSX-11M, but the relevant code is in
            different modules:-

            1)      [200,200]SGNMAS.CMD

            The  disk  UCBs  on  RSX-11M-PLUS contain all three values
            given  in  our  table  above, so only they, and not the DP
            driver, need be altered.

            After .DP30: change

                    .SETN ZN2 34200
            to
                    .SETN ZN2 172000
            and
                    .SETN ZN2 116100
            to
                    .SETN ZN2 175000
            and
                    .BYTE 10.,20.
            to
                    .BYTE 32.,5.

            2)      [12,10]SAVDP.MAC

            The  special  drivers for SAV and BOO have been split into
            separate modules, of which this one handles the RP11/SMD.

            After 1$: after DPCSR: change

                    DIV     #<10.*20.>,R2
            to
                    DIV     #<32.*5.>,R2
            and
                    DIV     #10.,R2
            to
                    DIV     #32.,R2

            This  file  should  then  be assembled and replaced in the
            relevant library, like so:-

            SET /UIC=[1,24]
            MAC SAVDP=[1,1]EXEMC/ML,[11,10]RSXMC/PA:1,[12,10]SAVDP
            LBR SAV/RP/-EP=SAVDP





            3)      [27,10]HRSIZ.MAC

            SAV  now  invokes  a module to do the disk sizing (sharing
            with the reconfigurer task).

            In the device table change

                    SIZE    0,116100,10.,20.,200.
            to
                    SIZE    0,175000,32.,5.,400.
            and
                    SIZE    1,34200,10.,20.,400.
            to
                    SIZE    1,172000,32.,5.,800.

            This  file  should  then  be assembled and replaced in the
            relevant library, like so:-

            SET /UIC=[1,24]
            MAC HRSIZ=[1,1]EXEMC/ML,[11,10]RSXMC,[27,10]HRPRE,HRSIZ
            LBR OLR/RP/-EP=HRSIZ

            4)      [12,10]DEVOV.MAC

            On  RSX-11M-PLUS  the  'DEV'  command displays the type of
            disk  drive  for  RP11s.  To get this to display correctly
            for SMDs:-

            After TYPE: change

                    RP02,RP03
            to
                    SM32,SM64

            and after DPSET: change

                    MOV     #RP02,R1
            to
                    MOV     #SM32,R1
            and
                    CMP     #40000.,U.CW3(R4)
            to
                    CMP     #175000,U.CW3(R4)
            and
                    MOV     #RP03,R1
            to
                    MOV     #SM64,R1

            This  file  should  then  be assembled and replaced in the
            relevant library, like so:-

            SET /UIC=[1,24]
            MAC DEVOV=[1,1]EXEMC/ML,[11,10]RSXMC/PA:1,[12,10]DEVOV
            LBR SAV/RP=DEVOV




                                CHAPTER 2

                          AMPEX Cartridge Drives

    a)      Hardware.

            The  AMPEX  Cartridge  Drives  are  identical  to the RK11
            Cartridge  Drives,  except  that  they  have twice as many
            Tracks  per  Surface.    The effect of this, as far as the
            software  is  concerned,  lies in the contents of the Disk
            Address Register.  For the RK11 bits 5 to 12 represent the
            cylinder  number, and bits 13 to 15 the drive number;  for
            the  AMPEX bits 5 to 13 represent the cylinder number, and
            bits 14 to 15 the drive number.

            As  SYSTIME  systems  are  sold  with  both RK11 and AMPEX
            drives  (though they must not be mixed on the same system)
            these  patches  are  not included in the basic software on
            the  distribution  disks  (though,  for  RSX-11M,  variant
            'AMPEX'  sources  exist  on the disk).  These patches have
            only been tested for RSX-11M.





    b)      RSX-11M.

            There are three changes necessary for the AMPEX mods:-

            1)      [11,10]DKDRV.MAC.

            As  with the SMDs this is the module that holds the driver
            for online operation.  For AMPEX drives:-

            After 20$: after DKINI: change

                    ASR     R2
            to
                    ASRB    R0

            Note  that  the  version  of this file on the Distribution
            Disk  has  this  change  conditionalised  under the symbol
            DK$AMX.

            2)      [12,10]SPCDRV.MAC.

            As  for SMDs this module contains a special driver for use
            by SAV and BOO.  For AMPEX drives:-

            After DKLLEN: change

                    BISB    DKFUN+1,$DKDAR+1
            to
                    ASLB    DKFUN+1
                    BISB    DKFUN+1,$DKDAR+1
                    ASRB    DKFUN+1

            and after DK2: change

                    BIC     #17777,RKDA(R5)
            to
                    BIC     #37777,RKDA(R5)

            and after DKEXIT: change

                    BIC     #17777,R4
            to
                    BIC     #37777,R4

            and change the first occurrence of

                    ROL     R4
            to
            ;       ROL     R4

            This  file  should  then  be assembled and replaced in the
            relevant library, like so:-

            SET /UIC=[1,24]
            MAC SPCDRV=[1,1]EXEMC/ML,[11,10]RSXMC/PA:1,[12,10]SPCDRV
            LBR SAV/RP/-EP=SPCDRV

            Note  that  on  the  Distribution Disk a re-assembled file
            exists  under  the name [1,24]SPCDRVAMX.OBJ which may just
            be replaced in the library.





            3)      The UCBs.

            As  for SMDs the UCB for an RK11/AMPEX contains the number
            of  blocks  on  the  device.  During System Generation the
            user should pause to edit the 'Executive files' and change
            the value in the UCB for each drive from 4800. to 9600.
            A comment is output by SYSGEN.CMD on the Distribution Disk
            just  before the 'Do you wish to edit any of the Executive
            files' question reminding the user of what to do for AMPEX
            drives.    (Note  that this comment will not appear if the
            SYSGEN is being done with a Saved Answer File.)





    c)      RSX-11M-PLUS

            Here again the changes are much the same as for RSX-11M.

            1)      [11,10]DKDRV.MAC

            After 15$: after DKINI: change

                    ASH     #13.,R1
            to
                    ASH     #14.,R1

            2)      [12,10]SAVDK.MAC

            After DKLLEN: change

                    BISB    DKFUN+1,$DKDAR+1
            to
                    ASLB    DKFUN+1
                    BISB    DKFUN+1,$DKDAR+1
                    ASRB    DKFUN+1

            and after DK2: change

                    BIC     #17777,RKDA(R5)
            to
                    BIC     #37777,RKDA(R5)

            and after DKEXIT: change

                    BIC     #17777,R4
            to
                    BIC     #37777,R4
            and
                    ASH     #-5,R4
            to
                    ASH     #-6,R4

            This  file  should  then  be assembled and replaced in the
            relevant library, like so:-

            SET /UIC=[1,24]
            MAC SAVDK=[1,1]EXEMC/ML,[11,10]RSXMC/PA:1,[12,10]SAVDK
            LBR SAV/RP/-EP=SAVDK





            3)      [27,10]HRSIZ.MAC.

            As for the SMDs this sets up the size in the UCBs.

            In the device table change:-

                    SIZE    0,4800.,12.,2,200.
            to
                    SIZE    0,9600.,12.,2,400.

            This  file  should  then  be assembled and replaced in the
            relevant library, like so:-

            SET /UIC=[1,24]
            MAC HRSIZ=[1,1]EXEMC/ML,[11,10]RSXMC,[27,10]HRPRE,HRSIZ
            LBR SAV/RP/-EP=HRSIZ

            4)      The UCBs.

            As for RSX-11M.




                                CHAPTER 3

                       SYSTIME MKII/MKIII Terminals

    a)      Hardware.

            The   full-duplex   terminal   driver   on   RSX-11M   and
            RSX-11M-PLUS  supports a wide range of terminal types, for
            use  in  identifying  terminals  (SET  /VT52), for setting
            default  terminal characteristics (SET /VT52=TT0:) and for
            'terminal-independent  cursor positioning'.  As the Cursor
            Positioning  Sequence for the SYSTIME MKII is different to
            other  terminals (30.,X+32.,Y+64.) extra code is needed to
            support  it.    In addition a SET /MKII interface has been
            added  to  MCR/TTDRV  to set the terminal to 80 characters
            wide, 25 lines long and to be a CRT.

            At this level SYSTIME MKIIIs are identical to MKIIs and so
            the  same interface can be used for each.  As most SYSTIME
            systems  are sold with SYSTIME terminals these changes are
            already  in  the  software  on  the Distribution Disk (for
            RSX-11M).  The changes have been tested for RSX-11M.





    b)      RSX-11M and RSX-11M-PLUS.

            Although  the patches have so far only been implemented on
            RSX-11M, the files are almost the same on RSX-11M-PLUS and
            so the changes required should be identical.  In each case
            four files need modification:-

            1)      [12,10]SPROVFDT.MAC (SPROV.MAC on RSX-11M-PLUS)

            This module processes the SET /MKII=TTn: command.

            In the table TRMTYP, before

                    .BYTE   0
            insert
                    .ASCIZ  /MKII/

            and at the end of the table KEYPRO

            insert
                    .WORD   SETMK2

            and at the end of the table TCODES

            insert
                    .WORD   T.USR0

            and immediately before

            SETVT1: INC     INDEX
            insert
            SETMK2: INC     INDEX

            During  System  Generation the Full-Duplex Terminal Driver
            versions  of  various  MCR  modules  are  replaced  in the
            relevant  library,  if  the FD driver was requested.  Thus
            this file should be re-assembled as follows:-

            SET /UIC=[1,24]
            MAC SPROVFDT=[1,1]EXEMC/ML,[11,10]RSXMC,[12,10]SPROVFDT
            MAC SDSOVFDT=[1,1]EXEMC/ML,[11,10]RSXMC,[12,10]SDSOVFDT
            MAC SETOVFDT=[1,1]EXEMC/ML,[11,10]RSXMC,[12,10]SETOVFDT
            PIP MCRTTFD.OBJ/NV=SPROVFDT.OBJ,SDSOVFDT.OBJ,SETOVFDT.OBJ

            2)      [12,10]SDSOVFDT.MAC (SDSOV.MAC on RSX-11M-PLUS)

            This module handles the MCR command SET /MKII.

            After T14: add

            T15:    .ASCIZ  /MKII/

            At the end of the table TTYTYP insert

                    .WORD   T15

            At the end of the table TCODES before

            TCODLN=.-TCODES
            insert
                    .WORD   T.USR0

            The file should be re-assembled as above.





            3)      [11,10]TTDAT.MAC

            This  module defines the types of terminals in the system,
            and their cursor positioning sequences.

            After SPDZ: change

            TTPHI   ==      T.SCR0
            to
            TTPHI   ==      T.USR0
            and
                    TERM    T.VT05  WID=72.,...,SCP=1,CUP=1
            to
                    TERM    T.VT05  WID=72.,...,SCP=1,CUP=0

            and after the line

                    TERM    T.SCR0  WID=132.,LEN=66.
            insert
                    TERM    T.USR0  WID=80.,LEN=25.,SCP=1,CUP=1

            and change the table CP1:: to

            CP1::
                    .BYTE   24.
                    .BYTE   30.,0,0

            4)      [11,10]TTSUB.MAC.

            This    is    the    module   that   actually   does   the
            'terminal-independent cursor psoitioning'.

            Change the code after CPOS1 to:-

                    ADD     #1001*40,R2
                    MOVB    R2,CP1+2
                    SWAB    R2
                    MOVB    R2,CP1+3
                    MOV     #3,R2
                    MOV     #CP1+1,R3
                    TST     (SP)+
                    CLZ
                    BPL     3$
                    DEC     R3
                    INC     R2
            3$:     RETURN




                                Systime Limited


                               Processing errors

 Page   Error description

    1   Cannot decipher Printer Control block keyword, block ignored