From the Wizzards Book of RSX MAGIC
                                  D. B. Curtis
                           SCIENCE APPLICATIONS, INC.
                                 Oak Brook, IL




        This  is  the  second  RSX  MAGIC  article.   Due  to  my   time
        limitations,  it  may  be the last unless the  wizards out there
        pitch in and help.

        This article describes processes that, if misused, may cause the
        destruction  of your operating system.  These methods should not
        be lightly used, they are provided to  help  solve  applications
        where  normal  RSX  methods  will  not work.  As with all magic,
        mistakes are dreadful!  (Remember the sorcerer's apprentice.)

        The last article described a method of sending ASTs to specified
        tasks.  This method was initially used in an error logging task.
        That error logger task is presented in this article.  I have not
        had  time  to  rework the code that sends ASTs so you get to see
        the original item.

        This task provides a  very  efficient,  general  purpose,  error
        display  task.  There is only a six word memory overhead at each
        error occurrence.   Essentially  this  is  done  by  dynamically
        adding  an  error  directive  to  the  executive.  The technique
        indicates  how  to  expand  the  functionality  of  the  RSX-11M
        executive without modification to the executive source.

        This particular version of the error task  was  written  for  an
        RSX-11S  system.   Therefore,  I did not use disk resident error
        messages.  However, it would be simple to add that capability.

        An example of the use of the error processor is shown below:


                MRKT$S  #1,#1,#1
                BCC     1$
                ERROR   MKTERR,-1,0,0
        1$:


        In this example you see  an  attempt  to  execute  a  mark  time
        directive.   If  the  directive fails, you want an error message
        and some attempt to recover from the error.  The recovery may be
        as  simple  as  aborting  the  task.  The error macro definition
        follows:


                                                                          Page 2



                .MACRO  ERROR,P1,P2,P3,P4
        ;
        ; MACRO TO SET UP INSTRUCTION BLOCK FOR ERROR MESSAGES
        ;
        ;       ERROR   KEY,TYPE,PRAM1,PRAM2
        ;
        ;               KEY <= 6 RAD50 CHARACTERS
        ;               TYPE = -1 FATAL ERROR
        ;                    = -2 FOR DELAYED RECOVERY
        ;                    = -3 FOR JUMP RECOVERY
        ;                    = 0 FOR MESSAGE ONLY
        ;       SEE DESCRIPTION IN ERRDIS MODULE
        ;

                .WORD   210             ; ERROR HANDLING INSTRUCTION
                .NCHR   TEMPN,P1
                .IIF LT 6-TEMPN .ERROR ; RAD50 NAME > 6 CHARACTERS
                .IF  LT 3-TEMPN
                .RAD50  /P1/
                .IFF
                .RAD50  /P1/
                .RAD50  /   /
                .ENDC
                .WORD   P2,P3,P4
                .ENDM   ERROR


                .MACRO  SAVRG
                JSR     R5,$SAVRG
                .ENDM


        The error control block looks like:



                -----------------------------------------
                |     OP CODE (210)                     |
                |---------------------------------------|
                |     FIRST 3 CHAR. OF RAD50 KEY        |
                |---------------------------------------|
                |     SECOND 3 CHAR. OF RAD50 KEY       |
                |---------------------------------------|
                |     FIRST PARAMETER                   |
                |---------------------------------------|
                |     SECOND PARAMETER                  |
                |---------------------------------------|
                |     THIRD PARAMETER                   |
                -----------------------------------------

        where:

        1.  The two word key is used to both identify the error, and  as
            a  key  into an expanded message table.  If a match is found
            in the message table, the message is printed in addition  to
            the normal information.


                                                                          Page 3


        2.  The first parameter specifies the type of error recovery  to
            perform.  This parameter takes the following values:

            1.  0 -- Message only.  The task continues  execution  after
                the error control block.  The second and third parameter
                contain data to be printed.  If the second parameter  is
                0,  R0 will be printed.  If the third parameter is 0, R5
                will be printed.

            2.  -1 -- Fatal error.  The  message  is  printed,  and  the
                erroring   task   is  aborted.   The  second  and  third
                parameters are treated as in the message only case.

            3.  -2 -- Recoverable error.  The message is printed and the
                task  continues  processing at the location specified in
                the second parameter.   The  first  byte  of  the  third
                parameter  is  the  number  of  seconds  to  wait before
                continuing, and the last byte of the third parameter  is
                the event flag to use while waiting.  If the seconds are
                zero, it will default to 1, if the event flag  is  zero,
                it will default to 1.

            4.  -3 -- Recoverable error.  The message is printed and the
                task  continues  processing at the location specified in
                the second parameter.  If parameter 3 is 0, R5  will  be
                printed.

            5.  If some other value than  the  ones  listed  above,  the
                error is printed, and the offending task is aborted.



        For example, you  would  use  -2  for  an  error  that  required
        operator intervention and -3 for an error exit from the routine.

        The error printout has the following form:
         
         'TSKNAM' PS = XXXXXX, PC = XXXXXX, DSW = XXXXXX
         ERROR 'KEYNAM', PRAMS = XXXXXX XXXXXX

        Where the XXXXXXs are  octal  numbers  for  the  values  of  the
        erroring  task.   KEYNAM is the keyword for the error and TSKNAM
        is the name of the task where the error occurred.

        If a message is associated with the error, the message  line  is
        printed  before  the  standard  display.   Again,  this could be
        easily modified for your special needs.



        1.0  DESCRIPTION OF THE CODE

        This section provides an overview of the operation of the  error
        logging task.


                                                                          Page 4


        The basic concept of the error logger is  to  allow  any  active
        task  to  display  an error without extra code in the task.  The
        error task is invoked by the  execution  of  a  PDP-11  reserved
        instruction.   The  error  logging  task  intercepts  the system
        illegal instruction processing and checks if the instruction  is
        the   one   specific  to  the  error  logging  system.   If  the
        instruction  is  not  the   error   logging   instruction,   the
        instruction  is  handled  in  the  normal manner, otherwise, the
        error logger is invoked.

        To install the illegal instruction  intercept,  the  error  task
        does  a  Connect-To-Interrupt directive to an unused vector.  At
        this time, some PIC code is inserted into the system  pool,  and
        the illegal instruction vector is pointed to the new code.  This
        code  examines  the  illegal  instruction  and  if  it  is   the
        instruction  specific to the error logger, will cause a transfer
        to the error logger via the vector specified by the  connect  to
        interrupt.   The code in the error logging task is simplified as
        the task is built as /PR:5.

        Information about the erroring task is gathered and  a  call  to
        $FORK2  transfers the task from interrupt level to system state.
        Here, information about the error is  placed  in  an  AST  block
        which is sent to the error logging task to be processed.



        2.0  DISCUSSION OF THE CODE

        The  complete  listing  of  the  error  routine   follows   this
        description.  Here I describe sections of the code.



        2.1  Initialization And Self Test

        The following is the initialization and self  test  sections  of
        the  error  logging  task.  The task initializes itself and then
        suspends.  If the task is resumed, it generates  a  sequence  of
        test error messages.


                                                                               Page 5



        CINT:   CINT$   ERRVEC,120000,ERRINT,ERRINI,PR7,ASTAD


        START:
                DIR$    #CINT           ; CONNECT TO THE VECTOR,
                BCC     10$             ; AND INIT IT, IF ERROR 
                IOT                     ; JUST CRASH

        10$:    SPND$S                  ; ELSE SUSPEND FOREVER
        ;
        ; IF THIS TASK IS RESUMED, IT WILL SELF TEST 
        ;
                ERROR   AAAAA,0,1,2     ; PRINT ERROR MESSAGE WITH 
                                        ;  DEFAULT PARAMETERS

                MOV     #3,R0
                MOV     #4,R5
                ERROR   BBBBB,0,0,0     ; PRINT ERROR MESSAGE 
                BR      30$             ; NEXT MESSAGE SHOULD BE DDDDD

        20$:    ERROR   CCCCC,-3,40$,6  ; NEXT MESSAGE WILL BE 
                                        ;    A DELAY MESSAGE

        30$:    ERROR   DDDDD,-3,20$,5  ; CCCCC IS NEXT MESSAGE

        40$:    ERROR   EEEEE,-2,50$,<<15*400>+5> ; CHECK FOR 5 SECOND DELAY

        50$:    ERROR   FFFFF,-2,60$,<<0*400>+0>  ; CHECK DEFAULT DELAY 
                                                  ;   AND EVENT FLAG

        60$:    ERROR   DONE,-3,10$,0   ; ALL DONE




        Note that the interrupt priority is 7 and that the base  address
        of the connect code is at the start of the task (120000).



        2.2  AST Handler

        The next section of code is the AST routine  that  displays  the
        errors.  This routine is easily modified for your special needs.
        One nice enhancement would be to  send  the  erroring  tasks  TI
        terminal  number to the AST routine so that the error would also
        be displayed on that terminal.


                                                                               Page 6


        ;
        ; INPUTS:
        ;       INFORMATION IS ON THE STACK, ALL REGISTERS MUST BE SAVED
        ;       THE INFORMATION  ON THE STACK IS:
        ;         2 WORDS OF RAD50 TASK NAME ISSUING THE INSTRUCTION
        ;         PS OF THAT TASK
        ;         PC OF THAT TASK
        ;         DSW OF THAT TASK
        ;         2 WORDS OF RAD50 ERROR KEYWORD
        ;         FIRST PARAMETER
        ;         SECOND PARAMETER
        ;       
        ;
        ; EQUATED SYMBOLS
        ;
        BEL = 7         ; ASCII CODE FOR BELL
                .ASECT
        . = 0
                                ; STACK PARAMETERS

        REGS:   .BLKW   6       ; R5-R0 R5 IS FIRST
        ERTNM:  .BLKW   2       ; 2 WORDS OF RAD50 TASK NAME FROM ERROR
        ETPS:   .BLKW   1       ; ERRORING TASKS PS
        ETPC:   .BLKW   1       ; ERRORING TASKS PC
        ETDSW:  .BLKW   1       ; ERRORING TASKS DSW
        EKEY:   .BLKW   2       ; 2 RAD50 WORDS WITH KEY NAME
        ETP1:   .BLKW   1       ; FIRST PARAMETER
        ETP2:   .BLKW   1       ; SECOND PARAMETER

                .PSECT
         

                .ENABL  LSB

        ASTAD:  
                .IRPC   REG,<012345>    ; SAVE THE REGISTERS
                MOV     R'REG,-(SP)
                .ENDM

        ;
        ; GET THE INFORMATION FROM THE INTERRUPT PART AND DISPLAY IT
        ;

                MOV     SP,R0           ; GET THE ADDR OF THE ERROR DATA BLOCK
                MOV     EKEY(R0),R1     ; GET THE FIRST WORD OF THE KEY
                MOV     #MSGKYS,R2      ; AND THE ADDRESS OF THE KEYS
        10$:    CMP     R1,(R2)         ; IS THE FIRST PART OF THE KEY THE SAME?
                BNE     20$
                                        ; HERE THE FIRST PART OF THE KEY MATCHES
                CMP     EKEY+2(R0),2(R2) ; DOES THE SECOND PART MATCH?
                BNE     20$             ; IF NE NO, SO CONTINUE
                BR      50$


        20$:    ADD     #6,R2           ; ADVANCE TO NEXT KEY
                TST     (R2)            ; CHECK NOT END OF KEYS
                BNE     10$             ; KEY NOT FOUND, => NO MESSAGE OTHER


                                                                               Page 7


                                        ;   OTHER THEN KEY ITSELF
        ;
        ; HERE, CONVERT KEY TO ASCII, AND PRINT IT AND OTHER VARIABLES
        ;
                .PSECT  MESFMT,RO,D
                .NLIST  BEX

        MG1:    .ASCII  <BEL><BEL>/'%2R' PS = %P, PC = %P, DSW = %P%N/
                .ASCIZ  /ERROR '%2R', PRAMS = %2P%N/
                .LIST   BEX
                .PSECT

        30$:    MOV     SP,R2           ; SAVE POINTER TO PARAMETERS
                ADD     #ERTNM,R2
                SUB     #200.,SP        ; SAVE SPACE FOR LINE ON STACK
                MOV     SP,R0
                MOV     SP,R5
                MOV     #MG1,R1         ; POINT TO FORMAT INFORMATION
                CALL    $EDMSG          ; FORMAT IT
                CMP     #200.,R1        ; CHECK STACK DIDN'T GET WIPED
                BGE     40$
                IOT

        40$:    QIOW$S  #IO.WBT,#TTLUN,#TTEV,,,,<R5,R1,#40>
                ADD     #200.,SP        ; CLEAN UP STACK
                BR      60$
        ;
        ; HERE PRINT MESSAGE, AND VARIABLES
        ;
        50$:
                MOV     4(R2),R1        ; GET ADDRESS OF MESSAGE
                MOVB    (R1)+,R2        ; GET SIZE OF MESSAGE
                QIO$S   #IO.WBT,#TTLUN,,,,,<R1,R2,#40>
                BR      30$

        60$:    .IRPC   REG,<543210>    ; RESTORE THE REGISTERS
                MOV     (SP)+,R'REG
                .ENDM

                ADD     #2*NUMPRM,SP    ; CLEAN OFF PARAMETERS
                ASTX$S

                .DSABL  LSB




        There isn't much magical about this routine, it is just a normal
        AST  receiver.   Well, almost normal as the number of parameters
        on the stack isn't a standard number, but if you read  the  last
        article you will not be surprised by that.


                                                                               Page 8


        2.3  Intercepting The Illegal Instruction Trap

        The next  routine  is  called  when  the  connect  to  interrupt
        directive   is   executed.   This  routine  is  responsible  for
        inserting some code into the system pool space and  intercepting
        the  illegal instruction trap.  The format of the intercept code
        in the pool follows the form that was described by  a  paper  in
        the  DECUS  proceedings<1>.  The error logger could just as well
        be inserted into the system with the ISF task  as  described  in
        that  paper.   However this task was developed for a stand alone
        RSX-11S task and needed to insert the code itself.








































------------------------------------

     <1>  Extending RSX-11M by Use of the Illegal Instruction Trap DECUS

          _________ _______ __ ___ __ ___ _______ ___________ ____
          PROCEEDINGS  Vol 6,  No. 2,  Pg. 467.   This paper describes a
          means of inserting code into the  system  pool.   It  is  good
          background reading for parts of this article


                                                                               Page 9


        ;+
        ;  **-ERRINI-CONNECT TO INTERRUPT ENABLE/DISABLE ROUTINE
        ;
        ; THIS ROUTINE ENABLES/DISABLES THE ILLEGAL INSTRUCTION INTERCEPT
        ; IF CARRY IS CLEAR, IT ENABLES, IF SET, IT DISABLES
        ; THIS MODULE ALLOCATES SOME POOL MEMORY, PLACES THE ILLEGAL INSTRUCTION
        ; INTERCEPT CODE INTO THE POOL AREA, MODIFIES XDT TO NOT PLAY WITH THE
        ; ILLEGAL INSTRUCTION TRAP VECTOR (ONLY IF XDT IS PRESENT) AND RETURNS.
        ; 
        ; THE DISABLE OF THIS OPERATION UNDOES ALL OF THE ABOVE
        ;
        ; INPUTS:
        ;       CARRY SET TO DETACH FROM VECTOR, CLEAR TO ATTACH TO VECTOR
        ;
        ; OUTPUTS:
        ;       NONE
        ;
        ; SIDE EFFECTS:
        ;
        ;    MODIFIED EXTERNALS
        ;
        ;    OTHER SIDE EFFECTS
        ;       POLADD,POLSIZ ARE SET TO THE ADDRESS OF THE POOL AREA, AND ITS SIZE
        ;       THE ILLEGAL INSTRUCTION TRAP VECTOR IS INTERCEPTED.
        ;
        ; REGISTER USAGE:
        ;       R1,R4,R5 ARE SAVED
        ;
        ;-


        ERRINI:
                BCC     10$             ;; CONNECT TO ILLEGAL INSTRUCTION VEC
                JMP     ABOPRO          ;; IF CARRY SET, DISCONNECT

        10$:    MOV     R5,-(SP)        ;; SAVE REGISTERS
                MOV     R4,-(SP)
                MOV     R1,-(SP)
                MOV     #EPOLCD-POOLCD,R1 ;; NEED TO ALLOCATE POOL SPACE TO PUT
                CALL    $ALOCB          ;; TRAP INTERCEPT CODE
                BCC     20$
                IOT                     ;; IF NO POOL SPACE, CRASH SYSTEM

        20$:    MOV     R0,POLADD       ;; SAVE ADDRESS OF ALLOCATED BLOCK
                MOV     R1,POLSIZ       ;; AND SIZE OF ALLOCATED BLOCK
                MOV     $TKTCB,MYTCBA   ;; AND WHILE AT IT, SET MY TCB ADDRESS

                MOV     #<EPOLCD-POOLCD>/2,R2   ;; GET THE NUMBER OF BYTES TO COPY
                MOV     #POOLCD,R3      ;; AND THE ADDRESS OF CODE TO MOVE
                                        ;; TOO THE POOL

        30$:    MOV     (R3)+,(R0)+     ;; DO THE MOVE
                SOB     R2,30$          ;; UNTIL FULLY COPIED

                MOV     POLADD,R0       ;; GET THE START ADDRESS OF POOL CODE
                ADD     #2,R0           ;; BUMP PAST THE "ILL"
                MOV     POLSIZ,(R0)+    ;; SAVE THE NUMBER OF BYTES IN CODE


                                                                              Page 10


                MOV     @#ILLVEC,(R0)+  ;; SAVE THE ORIGINAL VECTOR
                MOV     #NOP,(R0)       ;; TURN ON THE CODE

                MOV     #$XDT,R2        ;; CHECK IF XDT IS AVAILABLE
                BEQ     40$             ;; IF EQ NO

                SUB     #XDTFIX,R2      ;; CHECK IF XDT IS CONSISTENT
                CMP     @#ILLVEC,(R2)
                BNE     40$
                MOV     R0,(R2)         ;; ADJUST XDT

        40$:    MOV     R0,@#ILLVEC     ;; POINT ILLEGAL INSTRUCTION TRAP TO
                                        ;; THIS NEW CODE
                MOV     (SP)+,R1        ;; RESTORE REGISTERS
                MOV     (SP)+,R4
                MOV     (SP)+,R5
                RETURN                  ;; AND RETURN TO TASK



        This code inserts the PIC code that starts at  POOLCD  into  the
        system  pool.  It modifies XDT to allow executive debugging with
        this code inserted<2>.  The  code  that  is  inserted  into  the
        system  pool  examines  the  instruction that caused the illegal
        instruction trap.  If the instruction is recognised by the error
        system,   this  code  simulates  an  interrupt  via  the  unused
        interrupt vector that the error task connected  to.   Otherwise,
        the  illegal  instruction  is  passed  to  the  original illegal
        instruction trap handler.






















------------------------------------

     <2>  XDT resets the illegal instruction vector whenever it proceeds
          from   a  breakpoint.   Thus  resetting  our  intercept.   The
          modification  causes  XDT  to  bypass  resetting  the  illegal
          instruction vector.


                                                                              Page 11


        ;
        ; CODE THAT GETS LOADED INTO THE POOL
        ;  >>>>>> THIS CODE MUST BE PIC <<<<<
        ;
        POOLCD:
                .RAD50  /ILL/           ;;; SHOW THIS CODE IS ATTACHED TO THE 
                .WORD   0,0             ;;; ILLEGAL INSTRUCTION VECTOR
                RTI                     ;;; INITIALLY, TURN OFF CODE

        EP:     MOV     R5,-(SP)        ;;; SAVE R5
                MOV     2(SP),R5        ;;; AND GET TASK PC FROM STACK
                MFPI    -(R5)           ;;; GET THE INSTRUCTION THAT CAUSED THE TRAP
                CMP     (SP),#210       ;;; IS IT OUR INSTRUCTION?
                BEQ     100$

                ADD     #2,SP           ;;; NO! SO CLEAR THE STACK
                MOV     (SP)+,R5        ;;; RESTORE R5
                JMP     @EP-4           ;;; AND PROCESS NORMALLY
        ;
        ; HERE IT IS OUR ILLEGAL INSTRUCTION
        ;
        100$:   ADD     #2,SP           ;;; CLEAN THE STACK
                MOV     (SP)+,R5        ;;; RESTORE R5
                MOV     @#ERRVEC,-(SP)  ;;; AND JUMP VIA THE VECTOR WE ARE CONNECTED TO
                JMP     @(SP)+          ;;; POSITION INDEPENDENT INDIRECT JUMP
        EPOLCD:                         ;;; END OF THE CODE INSERTED INTO THE POOL




        The illegal  instruction  trap  vector  points  to  EP-2.   EP-4
        contains the address of the original service routine.

        If the error logging task exits, the modifications to  XDT  must
        be removed along with the intercept code from the system pool.


                                                                              Page 12


        ABOPRO:
                MOV     R1,-(SP)        ;; SAVE ITB POINTER
                MOV     @#ILLVEC,R0     ;; GET CURRENT VECTOR TO FIND OUR CODE
                MOV     -2(R0),@#ILLVEC ;; RESET THE ILLEGAL INSTRUCTION VEC
                MOV     #$XDT,R2        ;; RESET XDT
                BEQ     1$

                SUB     #XDTFIX,R2
                MOV     -2(R0),(R2)
        1$:     MOV     POLADD,R0       ;; GET THE ADDRESS OF THE POOL CODE
                MOV     POLSIZ,R1       ;; AND THE SIZE
                CALL    $DEACB
                MOV     (SP)+,R1        ;; RESTORE ITB POINTER
                RETURN



        The next routine contains a large amount of  magic.   It  copies
        the  error  parameter block from the user task and, if required,
        adjusts the  issuing  tasks  program  counter.   After  entering
        system  state  by a call to $FORK2, other actions on the issuing
        task are performed.  These  actions  are  aborting  or  delaying
        execution  of  the  issuing task.  Finally an AST is sent to the
        error logging task.


                                                                              Page 13


        ;+
        ;  **-ERRINT-PROCESSES ERROR INTERRUPTS
        ;
        ; THIS MODULE RECEIVES THE 210 INSTRUCTION CODE.
        ; IT SAVES THE ERROR BLOCK PARAMETERS, DOES ANY PROCESSING OF THE
        ; PARAMETERS (CHECKS WHAT TO DO WITH THE ISSUING TASKS PC).
        ; FORKS AND PLACES THE TASK IN THE APPROPRIATE STATE
        ;
        ; INPUTS:
        ;       R5 POINTS TO THE ITB
        ;       R4 IS SAVED AND MAY BE USED
        ;
        ; OUTPUTS:
        ;       NONE
        ;
        ; SIDE EFFECTS:
        ;
        ;    MODIFIED EXTERNALS
        ;
        ;    OTHER SIDE EFFECTS
        ;       MANY, TASK MAY BE ABORTED, MADE TO MARK TIME, TASKS PC MAY BE 
        ;       MOVED AS DIRECTED BY THE PARAMETERS ETC.
        ;
        ; REGISTER USAGE:
        ;       
        ;       R5 POINTS TO ITB
        ;       R4 IS SAVED AND MAY BE USED, ALL OTHER REGISTERS MUST BE SAVED AND
        ;       RESTORED
        ;
        ;-
         
        ;
        ; LOCAL DATA
        ;
        ERL1:   .WORD   0
        ERL2:   .WORD   0
        PER1:   .WORD   0
        PER2:   .WORD   0
        PER3:   .WORD   0



        ERRINT:                         ;;; HERE IF ILLEGAL INSTRUCTION
                                        ;;; FIRST 2 WORDS ARE RAD50 REP 
                                        ;;;   OF NAME OF ERROR
                MOV     10(SP),R4       ;;; GET PC OF TASK
                MFPI    (R4)+           ;;; GET FIRST WORD OF RAD50 ERROR
                MOV     (SP)+,ERL1      ;;;
                MFPI    (R4)+           ;;;
                MOV     (SP)+,ERL2      ;;;
                MFPI    (R4)+           ;;;
                MOV     (SP)+,PER1      ;;;
                MFPI    (R4)+           ;;;
                MOV     (SP)+,PER2      ;;;
                MFPI    (R4)+           ;;;
                MOV     (SP)+,PER3      ;;;



                                                                              Page 14


                TST     PER1            ;;; CHECK IF MESSAGE ONLY
                BMI     20$             ;;; IF MI NO

                MOV     R4,10(SP)       ;;; SET NEW PC AS ONLY MESSAGE IS REQUIRED
        10$:    CALL    @#$FORK2        ;;;
                CLR     (R3)            ;; CLEAR THE FORK BLOCK
                CALLR   SNDMSG          ;; AND SEND AST TO TASK STATE

        20$:    CMP     #-1,PER1        ;;; CHECK IF TO ABORT TASK
                BNE     40$             ;;; NE NO
                
        30$:    CALL    @#$FORK2        ;;;
                CLR     (R3)            ;; CLEAR THE FORK BLOCK
        32$:    MOV     #S.CABO,R0      ;; ABORTING FROM ILLEGAL INSTRUCTION
                CALL    $ABCTK          ;; ABORT THE CURRENT TASK
                CALLR   SNDMSG          ;; AND SEND AST TO TASK STATE

        40$:    CMP     #-2,PER1        ;;; CHECK IF OFFSET JMP
                BNE     50$             

                MOV     PER2,10(SP)     ;;; ADJUST PC
                CALL    @#$FORK2        ;;;
                CLR     (R3)            ;; CLEAR FORK BLOCK
                MOV     #2,-(SP)        ;; SET THE UNITS TO SECONDS
                MOVB    PER3,-(SP)      ;; GET THE NUMBER OF SECONDS TO WAIT
                BNE     41$             ;; CHECK SPECIFIED
                INC     (SP)            ;; DEFAULT IS 1

        41$:    CLRB    1(SP)           ;; MAX 255
                MOV     SP,R3           ;; POINT R3 TO BLOCK
                CALL    $CVRTM          ;; AND CONVERT THE TIME
                MOV     R0,2(SP)
                MOV     R1,(SP)
        42$:    MOVB    PER3+1,R0       ;; GET THE EVENT FLAG TO USE
                BNE     43$             ;; EVENT FLAG OF 0 IMPLIES DEFAULT
                INCB    PER3+1
                BR      42$

        43$:    MOV     $TKTCB,R5       ;; AND THE TCB OF THE CURRENT TASK
                CALL    $CEFI           ;; AND CONVERT TO MASK WORD AND ADDRESS
                BCC     45$
        44$:    ADD     #4,SP           ;; CLEAN UP STACK
                BR      32$

        45$:    CMPB    PER3,#64.       ;; CHECK IF GLOBAL EVENT FLAG
                BHI     44$             ;; IF SO GO TO 44 AND ABORT

                BIC     R0,(R1)         ;; CLEAR THE EVENT FLAG
                MOV     R0,-(SP)        ;; SAVE EVENT FLAG MASK WORD
                MOV     R1,-(SP)        ;; AND THE EVENT FLAG MASK ADDRESS
                MOV     T.PCB(R5),R4    ;; GENERATE POINTER TO TASK HEADER
                MOV     P.HDR(R4),R4
                INC     T.ST2(R5)       ;; PUT TASK IN WAIT FOR STATE
                MOV     2(SP),H.EFLM(R4) ;; SAVE WAIT FLAG 
                MOV     (SP),H.EFLM+2(R4)
                CALL    $SETRT          ;; SET SCHEDULE REQUEST
                MOV     #C.MRKT,R4      ;; MAKE CLOCK BLOCK A MARK TIME BLOCK


                                                                              Page 15


                CALL    $ALCLK          ;; ALLOCATE A CLOCK BLOCK
                MOVB    PER3+1,C.EFN(R0) ;; SAVE MARK TIME EVENT FLAG
                CLR     C.AST(R0)       ;; CLEAR THE AST ADDRESS
                MOV     (SP)+,C.DST(R0) ;; SET THE EVENT FLAG DESTINATION
                MOV     (SP)+,C.SRC(R0) ;; AND THE VALUE TO BE SET
                MOV     (SP)+,R2        ;; GET THE TIME TO WAIT
                MOV     (SP)+,R1
                CALL    $CLINS          ;; AND INSERT THE MARK TIME BLOCK IN THE
                CALLR   SNDMSG          ;; CLOCK QUEUE, AND SEND AST TO TASK STATE
                

        50$:    CMP     #-3,PER1        ;;; CHECK IF ABSOLUTE JMP
                BNE     30$             ;;;
                MOV     PER2,10(SP)     ;;;
                BR      10$             ;;;


        The call to SNDMSG just sends an AST to the user  mode  part  of
        the  task.   Starting  at  label 40$ is the code that causes the
        task to delay for a time.  One caution  here,  this  method  can
        only  be  used with an executing task that is in memory.  We are
        sure of that condition in this example, however other cases  may
        not be as simple.

        The next routine just sends the error  information  to  the  AST
        part of this task.  The method has already been explained in the
        last multi tasker.


                                                                              Page 16


        ;+
        ;  **-SNDMSG-SEND MESSAGE (VIA AST)
        ;
        ; THIS MODULE SENDS AN AST BLOCK TO THIS TASK.
        ; THE AST PARAMETERS ARE DESCRIBED IN THE AST RECEIVER MODULE
        ;
        ; INPUTS:
        ;       ERL1-PER3 -- INFORMATION FROM THE AST
        ;
        ; OUTPUTS:
        ;       GENERATES AN AST BLOCK WHICH IS QUEUED TO THE TASK
        ;
        ; SIDE EFFECTS:
        ;
        ;    MODIFIED EXTERNALS
        ;
        ;    OTHER SIDE EFFECTS
        ;
        ; REGISTER USAGE:
        ;       ALL REGISTERS ARE FREE TO BE USED
        ;
        ;-

        SNDMSG: 
                MOV     #<5+NUMPRM>*2,R1 ;; ALLOCATE AN AST BLOCK FOR ERRLOG
                CALL    $ALOCB          ;; ALLOCATE SOME POOL
                BCC     10$
                IOT                     ;; CRASH SYSTEM

        10$:    MOV     R0,R2           ;; COPY ADDRESS OF BLOCK
                MOV     R0,ASTADD       ;; SAVE ADDRESS OF BLOCK
                CLR     (R2)+           ;; CLEAR THE LINK
                MOV     R1,(R2)+        ;; SET IN SIZE OF BLOCK
                MOV     #<7+NUMPRM>*2,(R2)+ ;; SET NUMBER OF BYTES FOR STACK
                MOV     #ASTAD,(R2)+
                MOV     #NUMPRM,(R2)+   ;; SPECIFY THE NUMBER OF PARAMETERS
        ;
        ; LOAD STANDARD PARAMETERS
        ;
                MOV     $TKTCB,R0       ;; GET THE POINTER TO THE TCB
                MOV     T.NAM(R0),(R2)+ ;; GET THE TASK NAME
                MOV     T.NAM+2(R0),(R2)+
                MOV     22(SP),(R2)+    ;; GET THE TASK PS
                MOV     20(SP),(R2)+    ;; GET THE TASK NEW PC
                MFPI    @#$DSW          ;; GET THE USER DSW
                MOV     (SP)+,(R2)+
                MOV     ERL1,(R2)+      ;; SAVE ERROR LABEL
                MOV     ERL2,(R2)+
                
                TST     PER1            ;; CHECK FOR TYPE OF INFO TO TASK
                BNE     50$
        ;
        ; HERE FOR NORMAL MESSAGE NO TASK AFFECT
        ;
        20$:    MOV     PER2,(R2)+      ;; GET THE FIRST PARAMETER
                BNE     30$             ;; IF DEFAULT USE



                                                                              Page 17


                MOV     4(SP),-2(R2)    ;; R0 AS PARAMETER
        30$:    MOV     PER3,(R2)       ;; GET THE SECOND PARAMETER
                BNE     40$             ;; IF DEFAULT USE
                MOV     16(SP),(R2)     ;; R5 AS PARAMETER
        40$:    BR      70$

        50$:    CMP     PER1,#-1        ;; CHECK FOR FATAL ERROR
                BEQ     20$             ;;  TREAT AS NORMAL ERROR

                CMP     PER1,#-2        ;; CHECK FOR RECOVERABLE ERROR
                BNE     60$

                CLR     (R2)+           ;; IF RECOVERABLE ERROR, NO PARAMETER
                CLR     (R2)
                BR      70$

        60$:    CMP     PER1,#-3        ;; CHECK FOR RECOVERABLE ERROR
                BNE     20$
                CLR     (R2)+           ;; IF RECOVERABLE, NO PARAMETER 1
                BR      30$

        70$:    MOV     MYTCBA,R0       ;; GET TASK ERRDIS TASK TCB
                MOV     ASTADD,R1       ;; GET AST BLOCK ADDRESS
                CALLR   @#$QASTT        ;; AND PLACE ON AST QUEUE




        All that is left  is  to  see  how  the  table  of  extra  error
        information  lines  is  generated.   However,  this  is only the
        method I used for the RSX-11S system.  A unified error  file  is
        quite possible and is recommended.


                                                                              Page 18



        ;+
        ; FILE DESCRIPTION
        ;
        ;       THIS FILE CONTAINS ERROR MESSAGES 
        ;
        ;       THE MESSAGES ARE STORED UNSORTED IN THE FOLLOWING MANNER:
        ;
        ;               PSECT MSGKEY CONTAINS THE FOLLOWING STRUCTURE
        ;                       FIRST 3 CHARACTERS OF KEY
        ;                       SECOND 3 CHARACTERS OF KEY
        ;                       POINTER TO MESSAGE IN PSECT MSGMSG
        ;
        ;               THE KEYS ARE TERMINATED BY A KEY WITH SPACES AS THE
        ;               FIRST 3 CHARACTERS = IE 0
        ;
        ;               PSECT MSGMSG CONTAINS THE FOLLOWING STRUCTURE
        ;                       MESSAGE SIZE, MESSAGE
        ;
        ;-
        ;
        ;
                .MACRO  MAKMSG KEY,MES
                .PSECT  MSGMSG
                .NCHR   TEMSZ,<MES>
                TEMP = .
                .BYTE   TEMSZ
                .ASCII  /MES/
                .PSECT  MSGKEY
                .RAD50  /KEY/
                .WORD   TEMP
                .PSECT

                .ENDM   MAKMSG

                .PSECT  MSGKEY,RO,D
        MSGKYS::
                .PSECT  MSGMSG,RO,D
        MSG::
                .PSECT

                MAKMSG  AAAAA,<TEST MESSAGE>
                MAKMSG  <      >,<DONE>

                .PSECT  MSGMSG
                .EVEN

                .PSECT  MSGKEY
                .EVEN

                .PSECT


                .END
         


                                                                              Page 19


        The entire listing of the program, data file, build and assembly
        files follow.


;
; PREFIX FILE -- DEFF.MAC
;
	.MACRO 	ERROR,P1,P2,P3,P4
;
; MACRO TO SET UP INSTRUCTION BLOCK FOR ERROR MESSAGES
;
;	ERROR	KEY,TYPE,PRAM1,PRAM2
;
;		KEY <= 6 RAD50 CHARACTERS
;		TYPE = -1 FATAL ERROR
;		     = -2 FOR DELAYED RECOVERY
;		     = -3 FOR JUMP RECOVERY
;		     = 0 FOR MESSAGE ONLY
;	SEE DESCRIPTION IN ERRDIS MODULE
;

	.WORD	210		; ERROR HANDLING INSTRUCTION
	.NCHR	TEMPN,P1
	.IIF LT 6-TEMPN .ERROR ; RAD50 NAME > 6 CHARACTERS
	.IF  LT 3-TEMPN
	.RAD50	/P1/
	.IFF
	.RAD50	/P1/
	.RAD50	/   /
	.ENDC
	.WORD	P2,P3,P4
	.ENDM	ERROR

	.MACRO	SAVRG
	JSR	R5,$SAVRG
	.ENDM


 
	.TITLE	ERRDIS
	.IDENT	/X1.0/
;
;
; WRITTEN BY D.B.CURTIS
; SCIENCE APPLICATIONS, INC.
; 14-JUL-81
; ARGONNE NATIONAL LAB
;
;
; VERSION 01
; EDIT NUMBER = 0003
; FILE = ERRDIS.MAC
; EDITED BY: D.B.CURTIS  19 AUG 81  11:25
;
;
; MODIFICATIONS:
;
;+
; FILE DESCRIPTION
;
;	THIS TASK IS AN ERROR LOGGING TASK 
;	IT CAN BE USED WITH MOST OTHER RSX11-M/S FACILITIES IF THE ERROR 
;	MESSAGES AND KEYS ARE CHANGED.  THIS TASK INTERCEPTS THE ILLEGAL 
;	INSTRUCTION TRAP AND IS INVOKED BY THE 210 OP CODE.
;
;	INFORMATION FOLLOWS THAT OPCODE.  THIS INFORMATION DETERMINES HOW
;	THIS TASK PROCESSES THE ERROR.
;
;	THE MAIN PURPOSE OF THIS TASK IS TO DISPLAY ERRORS.  ITS SECONDARY
;	PURPOSE IS TO HELP RECOVER FROM THE ERRORS.  THIS MEANS THAT SOME
;	CONTROL OPERATIONS ARE PROVIDED.
;
;	THE ERROR CONTROL BLOCK LOOKS LIKE:
;
;		-----------------------------------------
;		|     OP CODE (210)			|
;		|---------------------------------------|
;		|     FIRST 3 CHAR. OF RAD50 KEY	|
;		|---------------------------------------|
;		|     SECOND 3 CHAR. OF RAD50 KEY	|
;		|---------------------------------------|
;		|     FIRST PARAMETER			|
;		|---------------------------------------|
;		|     SECOND PARAMETER			|
;		|---------------------------------------|
;		|     THIRD PARAMETER			|
;		-----------------------------------------
;
;	WHERE THE RAD50 KEY MUST MATCH WITH THE KEYS IN THE ERROR MESSAGE
;	TABLE. IF NO MATCH IS FOUND, THE KEY IS PRINTED.
;
;	THE FIRST PARAMETER SPECIFIES THE ACTION THIS TASK TAKES ON THE 
;	ISSUING TASK.  THIS PARAMETER TAKES THE FOLLOWING VALUES:
;
;		0 = MESSAGE ONLY, PROCESSING CONTINUES AFTER THE DATA BLOCK
;		THE SECOND AND THIRD PARAMETER CONTAIN DATA TO BE PRINTED
;		IF THE SECOND PARAMETER IS 0 R0 WILL BE PRINTED INSTEAD
;		IF THE THIRD PARAMETER IS 0, R5 WILL BE PRINTED INSTEAD
;
;		-1 = FATAL ERROR, THE MESSAGE IS PRINTED, AND
;		THE TASK IS ABORTED. THE SECOND AND THIRD PARAMETERS ARE
;		TREATED AS IN THE 0 CASE
;
;		-2 = RECOVERABLE ERROR, THE MESSAGE IS PRINTED. THE SECOND
;		PARAMETER CONTAINS THE ADDRESS TO SET THE PC TO.
;		THE FIRST BYTE OF THE THIRD PARAMETER IS THE NUMBER 
;		OF SECONDS TO WAIT, AND THE LAST BYTE OF THE THIRD 
;		PARAMETER IS THE EVENT FLAG TO USE WHILE WAITING.
;		IF THE SECONDS ARE ZERO, IT WILL DEFAULT TO 1, IF THE EVENT
;		FLAG IS ZERO, IT WILL DEFAULT TO 1.
;
;		-3 = RECOVERABLE ERROR, THE MESSAGE IS PRINTED. THE SECOND
;		PARAMETER CONTAINS THE ADDRESS TO SET THE PC TO.
;		IF PARAMETER 3 IS 0, R5 WILL BE USED AS AN ARGUMENT.
;
;	IF ANOTHER VALUE THE THE ONES LISTED ABOVE, THE ERROR IS PRINTED,
;	AN ERROR MESSAGE FROM THIS TASK IS PRINTED, AND THE OFFENDING
;	TASK IS ABORTED
;
;	YOU WOULD USE -2 FOR AN ERROR THAT REQUIRED OPERATOR INTERVENTION
;	YOU WOULD USE -3 FOR AN ERROR THAT COULD NOT BE TRIED AGAIN, 
;	AND JUMP TO AN ERROR EXIT
;
;
;
;-
	.MCALL	QIOW$S,CINT$,QIOW$,DIR$,ASTX$S,SPND$S,TCBDF$,ABODF$,HWDDF$
	.MCALL	QIO$S,CLKDF$,PCBDF$,HDRDF$

	ABODF$
	TCBDF$
	HWDDF$
	CLKDF$
	HDRDF$
	PCBDF$
;
; NUMBER OF PARAMETERS IN AST
;
NUMPRM = 9.


CINT:	CINT$	ERRVEC,120000,ERRINT,ERRINI,PR7,ASTAD
POLADD:	.WORD	0
POLSIZ:	.WORD	0
MYTCBA:	.WORD	0
ASTADD:	.WORD	0




START:
	DIR$	#CINT			; CONNECT TO THE VECTOR, AND INIT IT
	BCC	10$			; IF ERROR JUST
	IOT				; CRASH

10$:	SPND$S				; ELSE SUSPEND FOREVER
;
; IF THIS TASK IS RESUMED, IT WILL SELF TEST 
;
	ERROR	AAAAA,0,1,2		; PRINT ERROR MESSAGE WITH DEFAULT PARAMETERS

	MOV	#3,R0
	MOV	#4,R5
	ERROR	BBBBB,0,0,0		; PRINT ERROR MESSAGE WITH R0,R5 PARAM
	BR	30$			; NEXT MESSAGE SHOULD BE DDDDD

20$:	ERROR	CCCCC,-3,40$,6		; NEXT MESSAGE WILL BE A DELAY MESSAGE

30$:	ERROR	DDDDD,-3,20$,5		; CCCCC IS NEXT MESSAGE

40$:	ERROR	EEEEE,-2,50$,<<15*400>+5> ; CHECK FOR 5 SECOND DELAY

50$:	ERROR	FFFFF,-2,60$,<<0*400>+0>  ; CHECK DEFAULT DELAY AND EVENT FLAG

60$:	ERROR	DONE,-3,10$,0		; ALL DONE



;+
;  **-ASTAD-AST RECEIVER/ERROR DISPLAY MODULE
;
; THIS MODULE RECEIVES THE AST BLOCK FROM THE FORK CODE.
; IT TAKES THAT INFORMATION, SEARCHES FOR A MATCHING KEY IN THE 
; EXPANDED MESSAGE DATA AREA AND IF ONE IS FOUND THE EXPANDED MESSAGE
; IS WRITTEN OUT.  REGARDLESS OF WEITHER THE EXPANDED MESSAGE IS 
; FOUND, THE PARAMETERS IN THE AST BLOCK ARE WRITTEN OUT AS:
; 
; 'TSKNAM' PS = XXXXXX, PC = XXXXXX, DSW = XXXXXX
; ERROR 'KEYNAM', PRAMS = XXXXXX XXXXXX
; 
;
; INPUTS:
;	INFORMATION IS ON THE STACK, ALL REGISTERS MUST BE SAVED
;	THE INFORMATION  ON THE STACK IS:
;		2 WORDS OF RAD50 TASK NAME ISSUING THE INSTRUCTION
;		PS OF THAT TASK
;		PC OF THAT TASK
;		DSW OF THAT TASK
;		2 WORDS OF RAD50 ERROR KEYWORD
;		FIRST PARAMETER
;		SECOND PARAMETER
;	
; OUTPUTS:
;	NONE
;
; SIDE EFFECTS:
;
;    MODIFIED EXTERNALS
;
;    OTHER SIDE EFFECTS
;	STACK IS CLEANED, MESSAGE IS PRINTED
;
; REGISTER USAGE:
;	ALL REGISTERS SAVED
;
;-
;
; REFERENCED GLOBALS
;
	.GLOBL	$EDMSG 	; EDIT MESSAGE ( SYSTEM LIBRARY ROUTINES MANUAL)
	.GLOBL	MSGKYS	; ADDRESS OF THE ERROR KEY TABLE
	.GLOBL	TTLUN	; LUN OF THE TERMINAL I/O
	.GLOBL	TTEV	; EVENT FLAG FOR TERMINAL OPERATIONS
;
; EQUATED SYMBOLS
;
BEL = 7			; ASCII CODE FOR BELL
	.ASECT
. = 0
REGS:	.BLKW	6	; R5-R0 R5 IS FIRST
ERTNM:	.BLKW	2	; 2 WORDS OF RAD50 TASK NAME FROM ERROR
ETPS:	.BLKW	1	; ERRORING TASKS PS
ETPC:	.BLKW	1	; ERRORING TASKS PC
ETDSW:	.BLKW	1	; ERRORING TASKS DSW
EKEY:	.BLKW	2	; 2 RAD50 WORDS WITH KEY NAME
ETP1:	.BLKW	1	; FIRST PARAMETER
ETP2:	.BLKW	1	; SECOND PARAMETER

	.PSECT


	.ENABL	LSB

ASTAD:	
	.IRPC	REG,<012345>		; SAVE THE REGISTERS
	MOV	R'REG,-(SP)
	.ENDM

;
; GET THE INFORMATION FROM THE INTERRUPT PART AND DISPLAY IT
;

	MOV	SP,R0			; GET THE ADDR OF THE ERROR DATA BLOCK
	MOV	EKEY(R0),R1		; GET THE FIRST WORD OF THE KEY
	MOV	#MSGKYS,R2		; AND THE ADDRESS OF THE KEYS
10$:	CMP	R1,(R2)			; IS THE FIRST PART OF THE KEY THE SAME?
	BNE	20$
					; HERE THE FIRST PART OF THE KEY MATCHES
	CMP	EKEY+2(R0),2(R2)	; DOES THE SECOND PART MATCH?
	BNE	20$			; IF NE NO, SO CONTINUE
	BR	50$


20$:	ADD	#6,R2			; ADVANCE TO NEXT KEY
	TST	(R2)			; CHECK NOT END OF KEYS
	BNE	10$			; KEY NOT FOUND, => NO MESSAGE OTHER
					;   OTHER THEN KEY EITHER
;
; HERE, CONVERT KEY TO ASCII, AND PRINT IT AND OTHER VARIABLES
;
	.PSECT	MESFMT,RO,D
	.NLIST	BEX

MG1:	.ASCII	<BEL><BEL>/'%2R' PS = %P, PC = %P, DSW = %P%N/
	.ASCIZ	/ERROR '%2R', PRAMS = %2P%N/
	.LIST	BEX
	.PSECT

30$:	MOV	SP,R2			; SAVE POINTER TO PARAMETERS
	ADD	#ERTNM,R2
	SUB	#200.,SP		; SAVE SPACE FOR LINE ON STACK
	MOV	SP,R0
	MOV	SP,R5
	MOV	#MG1,R1			; POINT TO FORMAT INFORMATION
	CALL	$EDMSG			; FORMAT IT
	CMP	#200.,R1		; CHECK STACK DIDN'T GET WIPED
	BGE	40$
	IOT

40$:	QIOW$S	#IO.WBT,#TTLUN,#TTEV,,,,<R5,R1,#40>
	ADD	#200.,SP		; CLEAN UP STACK
	BR	60$
;
; HERE PRINT MESSAGE, AND VARIABLES
;
50$:
	MOV	4(R2),R1		; GET ADDRESS OF MESSAGE
	MOVB	(R1)+,R2		; GET SIZE OF MESSAGE
	QIO$S	#IO.WBT,#TTLUN,,,,,<R1,R2,#40>
	BR	30$

60$:	.IRPC	REG,<543210>		; RESTORE THE REGISTERS
	MOV	(SP)+,R'REG
	.ENDM

	ADD	#2*NUMPRM,SP		; CLEAN OFF PARAMETERS
	ASTX$S

	.DSABL	LSB



;+
;  **-ERRINI-CONNECT TO INTERRUPT ENABLE/DISABLE ROUTINE
;
; THIS ROUTINE ENABLES/DISABLES THE ILLEGAL INSTRUCTION INTERCEPT
; IF CARRY IS CLEAR, IT ENABLES, IF SET, IT DISABLES
; THIS MODULE ALLOCATES SOME POOL MEMORY, PLACES THE ILLEGAL INSTRUCTION
; INTERCEPT CODE INTO THE POOL AREA, MODIFIES XDT TO NOT PLAY WITH THE
; ILLEGAL INSTRUCTION TRAP VECTOR (ONLY IF XDT IS PRESENT) AND RETURNS.
; 
; THE DISABLE OF THIS OPERATION UNDOES ALL OF THE ABOVE
;
; INPUTS:
;	CARRY SET TO DETACH FROM VECTOR, CLEAR TO ATTACH TO VECTOR
;
; OUTPUTS:
;	NONE
;
; SIDE EFFECTS:
;
;    MODIFIED EXTERNALS
;
;    OTHER SIDE EFFECTS
;	POLADD,POLSIZ ARE SET TO THE ADDRESS OF THE POOL AREA, AND ITS SIZE
;	THE ILLEGAL INSTRUCTION TRAP VECTOR IS INTERCEPTED.
;
; REGISTER USAGE:
;	R1,R4,R5 ARE SAVED
;
;-
;
; REFERENCED GLOBALS
;
	.GLOBL	$ALOCB		; ALLOCATE CORE BLOCK
	.GLOBL	$TKTCB		; CURRENT TASK TCB ADDRESS
	.GLOBL	$DEACB		; DEALLOCATE CORE BLOCK
	.GLOBL	ERRVEC		; VECTOR TO SEND ERROR INSTRUCTION TOO
	.GLOBL	XDTFIX		; OFFSET FROM $XDT TO PATCH XDT ILLEGAL 
				; INSTRUCTION VECTOR RESET
	.GLOBL	$XDT 		; ENTRY POINT TO XDT
	.GLOBL	ILLVEC		; TRAP VECTOR ADDRESS FOR ILLEGAL INSTRUCTION



ERRINI:
	BCC	10$			;; CONNECT TO ILLEGAL INSTRUCTION VEC
	JMP	ABOPRO			;; IF CARRY SET, DISCONNECT

10$:	MOV	R5,-(SP)		;; SAVE REGISTERS
	MOV	R4,-(SP)
	MOV	R1,-(SP)
	MOV	#EPOLCD-POOLCD,R1	;; NEED TO ALLOCATE POOL SPACE TO PUT
	CALL	$ALOCB			;; TRAP INTERCEPT CODE
	BCC	20$
	IOT				;; IF NO POOL SPACE, CRASH SYSTEM

20$:	MOV	R0,POLADD		;; SAVE ADDRESS OF ALLOCATED BLOCK
	MOV	R1,POLSIZ		;; AND SIZE OF ALLOCATED BLOCK
	MOV	$TKTCB,MYTCBA		;; AND WHILE AT IT, SET MY TCB ADDRESS

	MOV	#<EPOLCD-POOLCD>/2,R2	;; GET THE NUMBER OF BYTES TO COPY
	MOV	#POOLCD,R3		;; AND THE ADDRESS OF CODE TO MOVE
					;; TOO THE POOL

30$:	MOV	(R3)+,(R0)+		;; DO THE MOVE
	SOB	R2,30$			;; UNTIL FULLY COPIED

	MOV	POLADD,R0		;; GET THE START ADDRESS OF POOL CODE
	ADD	#2,R0			;; BUMP PAST THE "ILL"
	MOV	POLSIZ,(R0)+		;; SAVE THE NUMBER OF BYTES IN CODE
	MOV	@#ILLVEC,(R0)+		;; SAVE THE ORIGINAL VECTOR
	MOV	#NOP,(R0)		;; TURN ON THE CODE

	MOV	#$XDT,R2		;; CHECK IF XDT IS AVAILABLE
	BEQ	40$			;; IF EQ NO

	SUB	#XDTFIX,R2		;; CHECK IF XDT IS CONSISTENT
	CMP	@#ILLVEC,(R2)
	BNE	40$
	MOV	R0,(R2)			;; ADJUST XDT

40$:	MOV	R0,@#ILLVEC		;; POINT ILLEGAL INSTRUCTION TRAP TO
					;; THIS NEW CODE
	MOV	(SP)+,R1		;; RESTORE REGISTERS
	MOV	(SP)+,R4
	MOV	(SP)+,R5
	RETURN				;; AND RETURN TO TASK

;
; CODE THAT GETS LOADED INTO THE POOL
;  >>>>>> THIS CODE MUST BE PIC <<<<<
;
POOLCD:
	.RAD50	/ILL/			;;; SHOW THIS CODE IS ATTACHED TO THE 
	.WORD	0,0			;;; ILLEGAL INSTRUCTION VECTOR
	RTI				;;; INITIALLY, TURN OFF CODE

EP:	MOV	R5,-(SP)		;;; SAVE R5
	MOV	2(SP),R5		;;; AND GET TASK PC FROM STACK
	MFPI	-(R5)			;;; GET THE INSTRUCTION THAT CAUSED THE TRAP
	CMP	(SP),#210		;;; IS IT OUR INSTRUCTION?
	BEQ	100$

	ADD	#2,SP			;;; NO! SO CLEAR THE STACK
	MOV	(SP)+,R5		;;; RESTORE R5
	JMP	@EP-4			;;; AND PROCESS NORMALLY
;
; HERE IT IS OUR ILLEGAL INSTRUCTION
;
100$:	ADD	#2,SP			;;; CLEAN THE STACK
	MOV	(SP)+,R5		;;; RESTORE R5
	MOV	@#ERRVEC,-(SP)		;;; AND JUMP VIA THE VECTOR WE ARE CONNECTED TO
	JMP	@(SP)+			;;; POSITION INDEPENDENT INDIRECT JUMP
EPOLCD:					;;; END OF THE CODE INSERTED INTO THE POOL

ABOPRO:
	MOV	R1,-(SP)		;; SAVE ITB POINTER
	MOV	@#ILLVEC,R0		;; GET CURRENT VECTOR TO FIND OUR CODE
	MOV	-2(R0),@#ILLVEC		;; RESET THE ILLEGAL INSTRUCTION VEC
	MOV	#$XDT,R2		;; RESET XDT
	BR	1$			;; IF IT IS IN THE SYSTEM

	SUB	#XDTFIX,R2
	MOV	-2(R0),(R2)
1$:	MOV	POLADD,R0		;; GET THE ADDRESS OF THE POOL CODE
	MOV	POLSIZ,R1		;; AND THE SIZE
	CALL	$DEACB
	MOV	(SP)+,R1		;; RESTORE ITB POINTER
	RETURN


;+
;  **-ERRINT-PROCESSES ERROR INTERRUPTS
;
; THIS MODULE RECEIVES THE 210 INSTRUCTION CODE.
; IT SAVES THE ERROR BLOCK PARAMETERS, DOES ANY PROCESSING OF THE
; PARAMETERS (CHECKS WHAT TO DO WITH THE ISSUING TASKS PC).
; FORKS AND PLACES THE TASK IN THE APPROPRIATE STATE
;
; INPUTS:
;	R5 POINTS TO THE ITB
;	R4 IS SAVED AND MAY BE USED
;
; OUTPUTS:
;	NONE
;
; SIDE EFFECTS:
;
;    MODIFIED EXTERNALS
;
;    OTHER SIDE EFFECTS
;	MANY, TASK MAY BE ABORTED, MADE TO MARK TIME, TASKS PC MAY BE 
;	MOVED AS DIRECTED BY THE PARAMETERS ETC.
;
; REGISTER USAGE:
;	
;	R5 POINTS TO ITB
;	R4 IS SAVED AND MAY BE USED, ALL OTHER REGISTERS MUST BE SAVED AND
;	RESTORED
;
;-
;
; REFERENCED GLOBALS
;
	.GLOBL	$FORK2 
 
;
; LOCAL DATA
;
ERL1:	.WORD	0		; TEMP STORAGE FOR ERROR KEY AND PARAMETERS
ERL2:	.WORD	0
PER1:	.WORD	0
PER2:	.WORD	0
PER3:	.WORD	0





ERRINT:					;;; HERE IF ILLEGAL INSTRUCTION
					;;; FIRST 2 WORDS ARE RAD50 REP OF NAME OF ERROR
	MOV	10(SP),R4		;;; GET PC OF TASK
	MFPI	(R4)+			;;; GET FIRST WORD OF RAD50 ERROR
	MOV	(SP)+,ERL1		;;;
	MFPI	(R4)+			;;;
	MOV	(SP)+,ERL2		;;;
	MFPI	(R4)+			;;;
	MOV	(SP)+,PER1		;;;
	MFPI	(R4)+			;;;
	MOV	(SP)+,PER2		;;;
	MFPI	(R4)+			;;;
	MOV	(SP)+,PER3		;;;

	TST	PER1			;;; CHECK IF MESSAGE ONLY
	BMI	20$			;;; IF MI NO

	MOV	R4,10(SP)		;;; SET NEW PC AS ONLY MESSAGE IS REQUIRED
10$:	CALL	@#$FORK2		;;;
	CLR	(R3)			;; CLEAR THE FORK BLOCK
	CALLR	SNDMSG			;; AND SEND AST TO TASK STATE

20$:	CMP	#-1,PER1		;;; CHECK IF TO ABORT TASK
	BNE	40$			;;; NE NO
	
30$:	CALL	@#$FORK2		;;;
	CLR	(R3)			;; CLEAR THE FORK BLOCK
32$:	MOV	#S.CABO,R0		;; ABORTING FROM ILLEGAL INSTRUCTION
	CALL	$ABCTK			;; ABORT THE CURRENT TASK
	CALLR	SNDMSG			;; AND SEND AST TO TASK STATE

40$:	CMP	#-2,PER1		;;; CHECK IF OFFSET JMP
	BNE	50$			

	MOV	PER2,10(SP)		;;; ADJUST PC
	CALL	@#$FORK2		;;;
	CLR	(R3)			;; CLEAR FORK BLOCK
	MOV	#2,-(SP)		;; SET THE UNITS TO SECONDS
	MOVB	PER3,-(SP)		;; GET THE NUMBER OF SECONDS TO WAIT
	BNE	41$			;; CHECK SPECIFIED
	INC	(SP)			;; DEFAULT IS 1

41$:	CLRB	1(SP)			;; MAX 255
	MOV	SP,R3			;; POINT R3 TO BLOCK
	CALL	$CVRTM			;; AND CONVERT THE TIME
	MOV	R0,2(SP)
	MOV	R1,(SP)
42$:	MOVB	PER3+1,R0		;; GET THE EVENT FLAG TO USE
	BNE	43$			;; EVENT FLAG OF 0 IMPLIES DEFAULT
	INCB	PER3+1
	BR	42$

43$:	MOV	$TKTCB,R5		;; AND THE TCB OF THE CURRENT TASK
	CALL	$CEFI			;; AND CONVERT TO MASK WORD AND ADDRESS
	BCC	45$
44$:	ADD	#4,SP			;; CLEAN UP STACK
	BR	32$

45$:	CMPB	PER3,#64.		;; CHECK IF GLOBAL EVENT FLAG
	BHI	44$			;; IF SO GO TO 44 AND ABORT

	BIC	R0,(R1)			;; CLEAR THE EVENT FLAG
	MOV	R0,-(SP)		;; SAVE EVENT FLAG MASK WORD
	MOV	R1,-(SP)		;; AND THE EVENT FLAG MASK ADDRESS
	MOV	T.PCB(R5),R4		;; GENERATE POINTER TO TASK HEADER
	MOV	P.HDR(R4),R4
	INC	T.ST2(R5)		;; PUT TASK IN WAIT FOR STATE
	MOV	2(SP),H.EFLM(R4)	;; SAVE WAIT FLAG 
	MOV	(SP),H.EFLM+2(R4)
	CALL	$SETRT			;; SET SCHEDIUAL REQUEST
	MOV	#C.MRKT,R4		;; MAKE CLOCK BLOCK A MARK TIME BLOCK
	CALL	$ALCLK			;; ALLOCATE A CLOCK BLOCK
	MOVB	PER3+1,C.EFN(R0)	;; SAVE MARK TIME EVENT FLAG
	CLR	C.AST(R0)		;; CLEAR THE AST ADDRESS
	MOV	(SP)+,C.DST(R0)		;; SET THE EVENT FLAG DESTINATION
	MOV	(SP)+,C.SRC(R0)		;; AND THE VALUE TO BE SET
	MOV	(SP)+,R2		;; GET THE TIME TO WAIT
	MOV	(SP)+,R1
	CALL	$CLINS			;; AND INSERT THE MARK TIME BLOCK IN THE
	CALLR	SNDMSG			;; CLOCK QUEUE, AND SEND AST TO TASK STATE
	

50$:	CMP	#-3,PER1		;;; CHECK IF ABSOLUTE JMP
	BNE	30$			;;;
	MOV	PER2,10(SP)		;;;
	BR	10$			;;;


;+
;  **-SNDMSG-SEND MESSAGE (VIA AST)
;
; THIS MODULE SENDS AN AST BLOCK TO THIS TASK.
; THE AST PARAMETERS ARE DESCRIBED IN THE AST RECEIVER MODULE
;
; INPUTS:
;	ERL1-PER3 -- INFORMATION FROM THE AST
;
; OUTPUTS:
;	GENERATES AN AST BLOCK WHICH IS QUEUED TO THE TASK
;
; SIDE EFFECTS:
;
;    MODIFIED EXTERNALS
;
;    OTHER SIDE EFFECTS
;
; REGISTER USAGE:
;	ALL REGISTERS ARE FREE TO BE USED
;
;-
;
; REFERENCED GLOBALS
;
	.GLOBL	$QASTT		; QUEUE AST TO TASK 



SNDMSG:	
	MOV	#<5+NUMPRM>*2,R1	;; ALLOCATE AN AST BLOCK FOR ERRLOG
	CALL	$ALOCB			;; ALLOCATE SOME POOL
	BCC	10$
	IOT				;; CRASH SYSTEM

10$:	MOV	R0,R2			;; COPY ADDRESS OF BLOCK
	MOV	R0,ASTADD		;; SAVE ADDRESS OF BLOCK
	CLR	(R2)+			;; CLEAR THE LINK
	MOV	R1,(R2)+		;; SET IN SIZE OF BLOCK
	MOV	#<7+NUMPRM>*2,(R2)+	;; SET NUMBER OF BYTES FOR STACK
	MOV	#ASTAD,(R2)+
	MOV	#NUMPRM,(R2)+		;; SPECIFY THE NUMBER OF PARAMETERS
;
; LOAD STANDARD PARAMETERS
;
	MOV	$TKTCB,R0		;; GET THE POINTER TO THE TCB
	MOV	T.NAM(R0),(R2)+		;; GET THE TASK NAME
	MOV	T.NAM+2(R0),(R2)+
	MOV	22(SP),(R2)+		;; GET THE TASK PS
	MOV	20(SP),(R2)+		;; GET THE TASK NEW PC
	MFPI	@#$DSW			;; GET THE USER DSW
	MOV	(SP)+,(R2)+
	MOV	ERL1,(R2)+		;; SAVE ERROR LABEL
	MOV	ERL2,(R2)+
	
	TST	PER1			;; CHECK FOR TYPE OF INFO TO TASK
	BNE	50$
;
; HERE FOR NORMAL MESSAGE NO TASK AFFECT
;
20$:	MOV	PER2,(R2)+		;; GET THE FIRST PARAMETER
	BNE	30$			;; IF DEFAULT USE

	MOV	4(SP),-2(R2)		;; R0 AS PARAMETER
30$:	MOV	PER3,(R2)		;; GET THE SECOND PARAMETER
	BNE	40$			;; IF DEFAULT USE
	MOV	16(SP),(R2)		;; R5 AS PARAMETER
40$:	BR	70$

50$:	CMP	PER1,#-1		;; CHECK FOR FATAL ERROR
	BEQ	20$			;;  TREAT AS NORMAL ERROR

	CMP	PER1,#-2		;; CHECK FOR RECOVERABLE ERROR
	BNE	60$

	CLR	(R2)+			;; IF RECOVERABLE ERROR, NO PARAMETERS
	CLR	(R2)
	BR	70$

60$:	CMP	PER1,#-3		;; CHECK FOR RECOVERABLE ERROR
	BNE	20$
	CLR	(R2)+			;; IF RECOVERABLE, NO PARAMETER 1
	BR	30$

70$:	MOV	MYTCBA,R0		;; GET TASK ERRDIS TASK TCB
	MOV	ASTADD,R1		;; GET AST BLOCK ADDRESS
	CALLR	@#$QASTT		;; AND PLACE ON AST QUEUE

	.END	START



	.TITLE	ERRDAT - ERROR DISPLAY DATA/MESSAGES
	.IDENT	/X1.0/
;
;
; WRITTEN BY D.B.CURTIS
; SCIENCE APPLICATIONS, INC.
; 14-JUL-81
; ARGONNE NATIONAL LAB
;
;
; VERSION 01
; EDIT NUMBER = 0001
; FILE = ERRDISDAT.MAC
; EDITED BY: D.B.CURTIS  14-JUL-81 10:11:46
;
;
; MODIFICATIONS:
;
;+
; FILE DESCRIPTION
;
;	THIS FILE CONTAINS ERROR MESSAGES 
;
;	THE MESSAGES ARE STORED UNSORTED IN THE FOLLOWING MANNER:
;
;		PSECT MSGKEY CONTAINS THE FOLLOWING STRUCTURE
;			FIRST 3 CHARACTERS OF KEY
;			SECOND 3 CHARACTERS OF KEY
;			POINTER TO MESSAGE IN PSECT MSGMSG
;
;		THE KEYS ARE TERMINATED BY A KEY WITH SPACES AS THE
;		FIRST 3 CHARACTERS = IE 0
;
;		PSECT MSGMSG CONTAINS THE FOLLOWING STRUCTURE
;			MESSAGE SIZE, MESSAGE
;
;-
;
;


	.MACRO	MAKMSG KEY,MES
	.PSECT	MSGMSG
	.NCHR	TEMSZ,<MES>
	TEMP = .
	.BYTE	TEMSZ
	.ASCII	/MES/
	.PSECT	MSGKEY
	.RAD50	/KEY/
	.WORD	TEMP
	.PSECT

	.ENDM	MAKMSG

	.PSECT	MSGKEY,RO,D
MSGKYS::
	.PSECT	MSGMSG,RO,D
MSG::
	.PSECT

	MAKMSG	AAAAA,<TEST MESSAGE>
	MAKMSG	<      >,<DONE>

	.PSECT	MSGMSG
	.EVEN

	.PSECT	MSGKEY
	.EVEN

	.PSECT


	.END


;
; ERRDATASM.CMD
;	COMMAND FILE TO ASSEMBLE ERRDIS AND ERRDAT MODULES
;
ERRDIS,ERRDIS=LB:[1,1]EXEMC/ML,[11,10]RSXMC,SY:[125,5]DEFF,ERRDIS
ERRDAT,ERRDAT=LB:[1,1]EXEMC/ML,[11,10]RSXMC,SY:[125,5]DEFF,ERRDAT


;
; ERRDISBLD.CMD
;	COMMAND FILE TO BUILD ERROR DISPLAY TASK
;
;   YOU MAY GET A UNDEFINED SYMBOLE '$XDT' IF XDT ISN'T IN THE SYSTEM.
;     THIS IS EXPECTED AND SHOULD NOT BE FIXED! (IT DEFAULTS TO 0)
;
ERRDIS/PR:5/-DA, = ERRDIS,ERRDAT
LB:[1,54]RSX11M.STB/SS
/
TASK = ERRDIS
;
; SET UP TERMINAL INTERACTION USE LUN4 AND EVENT FLAG 4
;
ASG = TI:4
GBLDEF = TTLUN:4
GBLDEF = TTEV:4
;
; OFFSET IN XDT TO INITIALLIZATION TABLE
;
GBLDEF = XDTFIX:300
;
; ILLEGAL INSTRUCTION TRAP VECTOR
;
GBLDEF= ILLVEC:10
;
; UNUSED VECTOR TO CONNECT TO
;
GBLDEF = ERRVEC:774
//