PROFILE V01.0

	THE PROFILE PACKAGE IS A SET OF TWO MACRO MODULES AND THIS
DOCUMENT THAT WILL ALLOW THE USER TO DETERMINE HOW OFTEN INSTRUCTION
MEMORY LOCATIONS ARE EXECUTED AT RUN(CRAWL) TIME AND A SUMMARY OF WHAT
INSTRUCTIONS WERE EXECUTED. THE 'MEASURE' MODULE IS TASK BUILT INTO
THE USERS PROGRAM TO RECORD THE MEMORY LOCATIONS AND INSTRUCTIONS
EXECUTED. THEN THE 'EVALUATE' PROGRAM IS RUN ON THE DATA GATHERED
AND A LISTING OF THE RESULTS IS GENERATED.



		MEASURE.MAC

	THIS MODULE IS TASK BUILT INTO THE TASK TO BE MEASURED AND
MAY NEED MODIFICATION AT BOTH THE SOURCE CODE LEVEL AND AT THE
TASK BUILD LEVEL TO PROPERLY OPERATE WITH THE USERS PROGRAM.

	THE SOURCE CODE CHANGES ARE AS FOLLOWS:

L.U.N. USEAGE.	THE MEASURE MODULE REQUIRES THAT TWO(2) DATA FILES
		BE OPEN DURING THE TAKING OF DATA. THE SOURCE CODE
		USES A DEFAULT OF LUN 1 AND LUN 2. IF THESE ARE IN
		CONFLICT WITH THE USEAGE OF THE USER PROGRAM, THESE
		CAN BE ALTERED BY CHANGEING THE SYMBOLS 'INSLUN'
		AND 'LOCLUN' THAT ARE DEFINED AT THE BEGINING
		OF THE SORCE CODE TO NONCONFLICTING VALUES.

EVENT FLAG USEAGE
		DATA GENERATED BY THE MEASURE MODULE IS KEPT ON DISK
		REQUIREING QIO'S TO RECOVER AND STORE BLOCKS OF
		COUNTERS. SINCE THIS MUST BE A SYNCHRONOUS OPERATION,
		QIOW$'S ARE USED SECIFYING AS DEFAULT EVENT FLAG
		20(10). IF THIS CONFLICTS WITH THE USER PROGRAM,
		THIS CAN BE MODIFIED BY CHANGEING THE SYMBOL
		'EVNFLG' AT THE BEGINING OF THE SOURCE TO A
		NON CONFLICTING ONE.



	DUE TO THE ADDITIONAL I/O REQUIRED BY THE MEASUREMENT ROUTINE,
SEVERAL MODIFICATIONS MAY BE REQUIRED AT TASK BUILD TIME.

OVERLAYS	THE MEASUREMENT ROUTINE IS CALLED VIA THE T-BIT
		TRAP AFTER THE EXECUTION OF EACH INSTRUCTION, SO
		IT MUST RESIDE IN THE ROOT SEGMENT. ALSO IT DOES'NT
		KNOW ABOUT OVERLAYS, SO THAT THE DATA ON LOCATION
		USEAGE IN THE OVERLAY AREA IS THE SUM OF ALL THE
		OVERLAYS USEAGE.

NUMBER OF ACTIVE FILES
		THE TASK BUILDER SETS UP THE TASK WITH A DEFAULT
		NUMBER OF ACTIVE FILES OF FOUR(4). SINCE THE MEASUREMENT
		ROUTINE REQUIRES 2, THIS LEAVES ONLY 2 FOR THE USER PROGRAM.
		THIS CAN BE EXTENDED BY 'ACTFIL=NNN' WHERE NNN ARE THE NUMBER
		OF ACTIVE FILES REQUIRED BY BOTH THE MEASUREMENT ROUTINE
		AND THE USER PROGRAM (SEE ALSO 'FCS I/O BUFFER SIZE')

DATA FILE DISK ASSIGNMENT
		THE MEASUREMENT ROUTINE GENERATES 3 DATA FILES ON
		THE DEFAULT DISK ASSIGNED TO THE LUN'S USED (DEFAULT
		ARE 1 AND 2 BUT CAN BE CHANGED IN THE SOURCE).
		TKB DEFAULT IS SY: BUT THE USER CAN MODIFY THIS AT
		TKB TIME BY THE USE OF 'ASG=XXN:1:2'.

FCS I/O BUFFER SIZE ($$FSR1)
		THE I/O REQUIREMENTS OF THE MEASUREMENT ROUTINE REQUIRE
		THE ASSIGNMENT OF SPACE FOR TWO(2) I/O BUFFERS. IF THE
		USER PROGRAM DOES NOT REQUIRE THIS AREA, THE MEASURE
		ROUTINE HAS BUILT IN TO IT THE TWO(2) BUFFERS THAT
		IT REQUIRES. IF THE USER PROGRAM DOES USE FCS I/O
		BUFFERS AND THE TOTAL BUFFER AREA IN $$FSR1 IS NOT
		SUFFICENT TO HANDLE ALL THE FILES THAT WILL BE OPEN
		SIMULTAINIOUSLY (TWO(2) OF WHICH ARE BY THE MEASUREMENT
		ROUTINE), THEN THE USER MUST EXTEND THEN SIZE OF THE
		I/O BUFFER AREA AT TKB TIME BY THE USE OF
		'EXTSCT=$$FSR1:XXXX'
		WHERE 'XXXX' IS THE TOTAL SIZE OF THE I/O BUFFER AREA
		IN OCTAL BYTES (THE REQUIREMENT FOR THE MEASUREMENT
		ROUTINE IS 2040(8) BYTES) (SEE ALSO 'NUMBER OF ACTIVE FILES').

HIGHEST LUN USED
		THE TASK BUILDER BY DEFAULT SETS THE HIGHEST LUN USEABLE
		BY A TASK TO 6. IF THE USER TASK OR MODIFIED MEASURE 
		ROUTINE REQUIRES A LUN HIGHER THAN 6, USE 'UNITS=N'
		WHERE 'N' IS THE HIHEST LUN USED.


	USER PROGRAM INTERFACE TO THE MEASUREMENT ROUTINE

	THE USER HAS FOUR(4) ENTRY POINTS THAT HE CAN CALL FROM
FORTRAN OR ASSEMBLY TO INTERFACE WITH THE MEASUREMENT ROUTINE.

	CALL	INIEXE			(JSR	PC,INIEXE)

		CALLED ONLY ONCE BY THE USER PROGRAM. THIS SUBROUTINE
		CREATES AND INITIALIZES THE THREE(3) DATA FILES USED
		IN THE PROFILE PACKAGE AND STARTS THE MEASUREMENT OF
		INSTRUCTION LOCATION'S EXECUTED AND INSTRUCTION TYPE
		EXECUTION SUMMARY (THE T-BIT TRAP IS ENABLED). THIS
		MUST BE THE FIRST EXECUTION MODULE SUBROUTINE CALLED
		AT RUN TIME.

	CALL TRMEXE			(JSR	PC,TRMEXE)

		CALLED ONLY ONCE BY THE USER PROGRAM. THIS SUBROUTINE
		TURNS OFF THE T-BIT TRAP, WRITES OUT ALL BUFFERS STILL
		IN MEMORY AND CLOSES ALL OPEN DATA FILES. THIS MUST BE
		THE LAST EXECUTION MODULE SUBROUTINE CALLED AT RUN TIME.

	CALL TROFF			(JSR	PC,TROFF)

		CALLED AT RUN TIME IN THE USER PROGRAM TO DISABLE MEASUREMENT
		OF PROGRAM ACTIVITY.

	CALL TRON			(JSR	PC,TRON)

		CALLED AT RUN TIME IN THE USER PROGRAM TO RE-ENABLE MEASURMENT
		OF PROGRAM ACTIVITY.



	FOR MOST USER PROGRAMS, THE ONLY REQUIREMENTS WILL BE TO DO
A 'CALL INIEXE' AS THE FIRST EXECUTEABLE INSTRUCTION OF THE PROGRAM,
AND A 'CALL TRMEXE' AS THE LAST.


	THE MEASUREMENT ROUTINE CREATES 3 DATA FILES FOR THE EVALUATION
PROGRAM.

MEASURE.DAT	A ONE BLOCK LONG FILE THAT CONTAINS THE FOLLOWING INFORMATION
		FOR THE EVALUATION PROGRAM:
		TASK NAME (AS INSTALLED)
		TASK START TIME
		TASK START DATE

LOCTCTR.DAT	A 256(10) CONTIGUOUS BLOCK LONG FILE THAT CONTAINS I*4
		COUNTERS, ONE FOR EACH VIRTUAL WORD ADDRESS IN THE USERS
		PROGRAM. AT THE COMPLETION OF EXECUTION OF EACH INSTRUCTION,
		THE T-BIT TRAP IS TAKEN, AND THE LOCATION OF THE NEXT
		INSTRUCTION TO BE EXECUTED IS OBTAINED FROM THE STACK,
		AND THE CORRESPONDING COUNTER FOR THAT LOCATION IS
		INCREMENTED.

INSTCTR.DAT	A 512(10) CONTIGUOUS BLOCK  LONG FILE THAT CONTAINS I*4
		COUNTERS, ONE FOR EACH OF THE POSSABLE 65536(10)
		INSTRUCTION BIT PATTERNS. AT THE COMPLETION OF EACH
		INSTRUCTION, THE T-BIT TRAP IS TAKEN, AND THE NEXT
		INSTRUCTION TO BE EXECUTED IS OBTAINED AND THE 
		CORRESPONDING COUNTER FOR THAT BIT PATTERN IS INCREMENTED.



		EXECUTION TIME/SPACE OVERHEAD

	IT MUST BE NOTED, THAT EVEN WITH THE USE IN THE MEASUREMENT ROUTINE
OF QIO'S RATHER THAT GET'S AND PUT'S, AND THE BUFFERING OF FOUR(4) LOCATION
TABLES AND EIGHT(8) INSTRUCTION TABLES IN MEMORY TO REDUCE I/O, THE 
EXECUTION SPEED OF THE USER PROGRAM IS SEVERELY DEGRADED. A SMALL FORTRAN
TEST PROGRAM SHOWED AN INCREASE OF EXECUTION TIME OF AS MUCH AS 130:1
OVER THE NON MEASURED EXECUTION TIME. THIS NUMBER IS SUPPLIED ONLY AS A
ROUGH GUIDE AND NOT AS AN EXACT MEASURE OF ITS EFFECT ON THE RUN( OR
IN THIS CASE CRAWL) TIME OF A USER PROGRAM.

	THE MEMORY REQUIREMENTS OF THE MEASUREMENT MODULE ARE AS FOLOWS:

	CODE/INTERNAL BUFFERS		3994(10) WORDS
	$$FSR1 (FCS I/O BUFFERS)	 528(10) WORDS
	$$FSR2				  34(10) WORDS
	$$RESL (FCS/SYSLIB ROUTINES)	2508(10) WORDS
					______________
					7064(10) WORDS

NOTE THAT IF THE USER PROGRAM DOES ANY FILE STRUCTURED I/O, THE
FCS/SYSLIB ROUTINES IN $$RESL ARE USED BY BOTH THE USER PROGRAM
AND THE MEASUREMENT ROUTINE.


		EVALUATION PROGRAM
		
	THE EVALUATION PROGRAM TAKES THE 3 DATA FILES GENERATED
BY THE MEASUREMENT ROUTINE (DELETEING THEM WHEN DONE) AND GENERATES
A LIST FILE SHOWING THE USER PROGRAM RUN TIME EXECUTION PROFILE.
THE LIST FILE GENERATED HAS FOUR(4) PARTS:


	PROGRAM INSTRUCTION LOCATION USEAGE COUNT BY LOCATION

	THIS SECTION MAKES ONE PASS THROUGH THE LOCATION COUNTER DATA FILE
AND PRINTS OUT IN INCREASING LOCATION ADDRESS ALL INSTRUCTION ADDRESSES
WITH NON-ZERO USEAGE COUNT, GIVEING THE OCTAL ADDRESS AND THE DECIMAL
USAGE COUNT.


	PROGRAM INSTRUCTION LOCATION USEAGE COUNT BY COUNT

	THIS SECTION IS THE RESULT OF A SORT DONE ON THE DATA FROM THE
PREVIOUS SECTION. ALL ADDRESSES WITH NON-ZERO COUNTS ARE PRINTED OUT
IN ORDER OF DECREASING USEAGE COUNTS. THE FORMAT BEING THE SAME AS THE
FIRST SECTION OF THE PRINTOUT.


	PROGRAM INSTRUCTION USEAGE TABLE

	THIS SECTION PRINTS OUT INFORMATION ON ALL THE INSTRUCTIONS
EXECUTED BY THE USER PROGRAM. FOR EACH INSTRUCTION EXECUTED, THE FORMAT
IS AS FOLLOWS:

INSTRUCTION MNEMONIC		NUMBER OF TIMES USED(DECIMAL)

E.G.

EMT				1020


DEPENDING ON THE INSTRUCTION, ONE OR MORE OF THE FOLLOWING TABLES ARE
PRINTED OUT FOLLOWING THE INSTRUCTION NAME AND TOTAL COUNT:

REGESTER OR ACCUMULATOR ONLY MODE INSTRUCTION

		R0	R1	R2	R3	R4	R5	R6	R7
		COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT


FULL SOURCE AND/OR INSTRUCTION MODE INSTRUCTION


		R0	R1	R2	R3	R4	R5	R6	R7
MODE  R		COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT
MODE (R)	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT
MODE (R)+	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT
MODE @(R)+	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT
MODE -(R)	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT
MODE @-(R)	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT
MODE X(R)	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT
MODE @X(R)	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT	COUNT

	(ANY MODE WHERE NO REGESTER IS USED, IS NOT PRINTED OUT)
WHERE THE INSTRUCTION IS A FULL SOURCE AND DESTINATION REGESTER OPERAND
TWO(2) TABLES ARE GENERATED, ONE EACH FOR SOURCE AND DESTINATION.


	PROGRAM SUMMARY

	THE FINAL PART OF THE LISTING IS A SUMMARY OF THE ENTIRE USER
PROGRAM. THIS INCLUDES THE TOTAL NUMBER OF INSTRUCTIONS EXECUTED,
A PAIR OF TABLES LAIKE THOSE IN PART THREE OF THE LISTING SHOWING
FOR SOURCE AND DESINATION USEAGE THE CPU REGESTERS AND MODES OF USE,
AND (IF ANY ARE USED) THE SOURCE AND DESTINATION UESAGES OF ANY
FPU ACCUMULATORS.


	RUNNING THE EVALUATION PROGRAM

	NO USER INTERACTION IS REQUIRED IN THE OPERATION OF THE
EVALUATION PROGRAM ONCE THE COMMAND 'RUN EVALUATE' HAS BEEN GIVEN.
THE PROGRAM AUTOMATICALY LOOKS FOR THE THREE(3) DATA FILES GENERATED
BY THE MEASUREMENT ROUTINE (DELETEING THEM WHEN DONE), GENERATEING
A LIST FILE OF THE RESULTS ('EVALUATE.LST') AND SPOOLING IT WHEN
DONE.


	BUILDING THE PROFILE PACKAGE

	THE MEASURE MODULE (MODIFIED AS NEEDED BY THE USER TO BE
COMPATABLE WITH THE LUN AND EVENT FLAG USEAGE OF HIS PROGRAM) IS
ASSEMBLED

MAC MEASURE=MEASURE

IT CAN THEN BE TASK BUILT INTO THE USER TASK WITH ANY REQUIRED OPTIONS
AS OUTLINED EARLIER IN THIS DOCUMENT.


	THE EVALUATION PROGRAM NEED ONLY BE BUILT ONCE.

MAC EVALUATE=EVALUATE
TKB EVALUATE/FP=EVALUATE

NOTE THE '/FP' AS PART OF THE PRINT OUT FORMATTING USES THE FPU.


		FOR ANY QUESTIONS, BUG REPORTS, IMPROVEMENTS CONTACT

		MICHAEL N. LEVINE
		CODE 3513
		NAVAL WEAPONS CENTER
		CHINA LAKE
		CALIFORNIA
		93555

		(714) 939-2417
		 AVN  437-2417