9
/81


















                               PRM-11 U
SER'S GUIDE

                         OMSI PASCAL INTERFACE TO RMS-11












                                Kenneth G. Tibesar
               
     3M Engineering Systems and Technology Labs
                            St.
 Paul, Minnesota 55144



Pascal Record Management User's Manual               
             PAGE 2
Table Of Contents


          1.0 Introduction To PRM
 
           1.1 PRM Design
            1.2 User Interface
            1.3 File 
Operations
            1.4 Record Operations
            1.5 RFA
            
1.6 Memory Requirements
          2.0 Preparing for PRM
            2.1 Pre-de
fined Data Structures
            2.2 Control Buffers
              2.2.1 RmsF
ileDesc - File Description
              2.2.2 RetRecord - Record Retrieval
  
            2.2.3 StoRecord - Record Storage
              2.2.4 IdxKeyDesc - I
ndexed Key Description
            2.3 Record Buffers
              2.3.1 Non-
Shared Buffers
              2.3.2 Shared Buffers
            2.4 Key Buffers


            2.5 PRM External Calls
            2.6 Rms-11 Initialization
    
        2.7 Task Build
            2.8 User Space Optimization
            2.9
 PRM Pit-Falls 
          3.0 Detailed Description of PRM Buffers
            
3.1 RmsFileDesc - File Description
            3.2 RetRecord - Record Retrieval

            3.3 StoRecord - Record Storage
            3.4 IdxKeyDesc - Index
ed Key Description
            3.5 User Defined Record Buffers
          4.0 D
etailed Description of PRM Routines
            4.1 General Use
            4.
2 File Access and Creation
              4.2.1 PRMClo
              4.2.2 PRMC
re
              4.2.3 PRMKey
              4.2.4 PRMOpe
            4.3 Reco
rd Retrieval and Storage
              4.3.1 PRMDel
              4.3.2 PRMFre

              4.3.3 PRMRet
              4.3.4 PRMSto
           
         
 Appendix A  PRM program example - Access an existing RMS files
          Appen
dix B  PRM program example - Dynamic creation of an RMS
           indexed file

          Appendix C  PRM example command and overlay descriptor files
      
    Appendix D  PRM Error Codes
           



Pascal Record Management User's
 Manual                            PAGE 3
Preface


          PREFACE

   
            Record Management Services (RMS-11) is a software package
         
 written   and  supported  by  DEC.   The  package  is  a  data
          manag
ement tool that supports sequential, relative and indexed
          (ISAM) file
s.

               Pascal Record  Management  (PRM-11)  is  a  non-supported
          interface  developed  by 3M Engineering and Systems Technology
      
    Labs.  PRM was developed as an interum until the  OMSI  Pascal
          Co
mpiler directly supports RMS-11.  

               PRM was developed and teste
d using V1.2G of  OMSI  Pascal
          and  DEC RSX-11M+ operating system.  K
nown problems will occur
          when using OMSI Pascal V1.2H due to changes 
in  initialization
          procedures.   Version 2 of OMSI Pascal can be used
 only if the
          Version 1 switch is used.

               Comments and
 questions concerning PRM should be  directed
          in writting to:
      
     
                            Kenneth Tibesar
                            
3M Center, Bldg. 518-1
                            St. Paul, Minnesota 55144
 
          














                         CHAPTER 1

     
               Introduction to PRM




               PRM-11 is a set of ro
utinnes written in OMSI Pascal  with
          in-line  MACRO-11  code to inter
face to RMS-11.  DEC supported
          high level languages interface to RMS-
11 by  using  key  words
          supported  by  the language compiler.  The p
resent versions of
          OMSI Pascal for the PDP-11 does not support RMS-11
  interface.
          PRM  provides  the  interface via a set of external proc
edures
          that are similiar to the key words used by DEC languages.  PRM

          routines  are  called  by the user code when RMS-11 operations
    
      are required.  The PRM routines are linked to  the  user  code
          
during the task build.



          1.1  PRM Design


               PRM 
routines  use  DEC  supported  MACRO-11  routines  to
          perform  RMS-11
  operations.  RMS-11 requires attribute blocks
          describing the file  
(FAB)  and  record  (RAB).   PRM  defines
          fields  within  the  attrib
ute  blocks.  This allows Pascal to
          directly control the contents of 
the files RABs and FABs.  The
          contents of the RABs and FABs are indir
ectly controlled by the
          PRM user by loading pre-defined buffers and u
sing one  of  the
          PRM external procedures.

               User buf
fers required by PRM routines  are  allocated  in
          the  user  space.  
The user defines only the number of buffers
          required for the applicat
ion.  The buffers are loaded  by  the
          PRM  user  to  indicate file or
 record access parameters.  The
          buffers are also used by  PRM  as  wo
rking  space.   By  using
          buffers  allocated  globally (from the heap
), PRM can preserve
          variables between PRM calls.

               No
rmally, RMS-11 requires the user to reserve POOL space.
          The  POOL  sp
ace  is  used  by  RMS  internal  code as control
          structures known as
 BDB's  (Buffer  Descriptor  Blocks).   The
          POOL  space  has  to  be 
 allocated  based  on  the  number of
          simultaneously opened files.  T
his design  would  wastes  user
          space that cannot be reclaimed even t
hough the file is closed.



Pascal Record Management User's Manual            
              PAGE 1-2
Introduction to PRM


          To avoid this loss of
 valuable  user  space,  PRM  dynamically
          allocates  and  deallocates
 the space when required by RMS-11.
          RMS-11 allows the MACRO-11 progra
mmer to specify  a  GSA  (Get
          Space)  routine.   The PRM GSA routine 
simply calls the Pascal
          Run-Time-System NEW and DISPOSE routines to m
anage HEAP space.
          RMS-11  uses  the  declared  GSA  routine  when it 
requires or
          releases space.  Space is not used until a file is opened
  and
          returned to the Pascal heap when the file is closed.

       
        PRM  was  modled  after  syntax  used  by  existing   DEC
          sup
ported  languages  that interface to RMS-11.  The following
          is a list
 of PRM and high level language comparisons:

               1.  DEC - Compile
rs support commands that perform  RMS-11
                   file and record ope
rations.  

                        PRM - External procedures linked to  the  
Pascal
                   program perform RMS-11 file and record operations.



               2.  DEC- Descriptive  key  words  are  used  with  RMS-11
     
              commands to specify attributes of the file and record
           
        operations.

                        PRM - Descriptive field names are
 used  to  load
                   records  passed  to  the  external  procedur
es.   The
                   record fields  specify  attributes  of  the  file 
 or
                   record operation.

               3.  DEC - A completi
on code  indicating  the  success  of
                   failure  of  each  RMS
 operation is made available to
                   the user.  The completion co
de is available thru  the
                   use   of   a  reserved  word.   Op
timize  user  space
                   utilization if necessary.

           
    4.  PRM - A completion code in  returned  with  each  PRM
                 
  call.   The  code  is  the standard RMS-11 completion
                   code
.  In addition, PRM provides debugging completion
                   codes for 
the PRM user.




          1.2  User Interface


               The PRM
 interface to OMSI Pascal uses the Pascal internal
          record  structure 
 to  pass  data.   Pre-defined  records  are
          included in the TYPE dec
laration of the User  Pascal  program.
          The Pascal programmer determin
es the operation to be performed
          (open, close, get record,  etc.)  an
d  loads  the  appropriate
          record  buffer.   Once loaded, the reocrd 
address is passed to
          the specific PRM routine that  performs  the  fi
le  or  record
          operation.   The  PRM  routines  load the RMS attribut
e blocks



Pascal Record Management User's Manual                          PAG
E 1-3
Introduction to PRM


          (RAB and/or FAB) with the control code
s necessary  to  satisfy
          the  user  request.  If data is to be stored
 or retrieved, the
          User Pascal program is also required to pass the a
ddress of  a
          data buffer.  

               In addition to control 
 and  data  buffer  addresses,  an
          address  of  a  status  buffer is 
required with all PRM calls.
          The status buffer is loaded with a compl
etion code.  The  code
          is a standard MACRO-11 RMS success/error code 
(refer to RMS-11
          User's Manual, Appendix B).   In  additionn  PRM  wi
ll  return
          debugging  error  codes for the PRM user.  PRM error codes
 are
          only generated due to PRM user  procedural  error.   Refer  to
          Appendix D of this document.

               The user should check t
he completion code following  each
          PRM  call.   If  the  file  is  no
t opened properly, no record
          operations should be performed.  If the 
user  continues  after
          an error in a file open or creation, PRM will 
catch the error.
          All record operations on an improperly opened or cre
ated  file
          are prohibited.



          1.3  File Operations




               There are four file  operation  primitives  provided.   A
     
     buffer  of  TYPE  RmsFileDesc  is  used  with all the PRM file
          r
outines.  The PRM user must allocate a buffer  of  this  TYPE
          for eac
h simultaneously open file.  

               The buffer is loaded by the PRM 
user to describe the file
          to  be opened or created.  Once the file is
 open, the contents
          of this buffer provides space for the file  attri
butes  blocks
          (FAB  and  RAB).   The  attributes  blocks  are  loaded
 by PRM
          routines to indicate PRM User  requests  to  RMS-11  routines
.
          All  PRM  record  operations  require the PRM User to pass the
   
       address of the RmsFileDesc buffer.  This inidicates to PRM the
         
 file  to  be accessed.  Since space is allocated in user space
          for t
he file attributes blocks, file data is preserved between
          PRM calls.



               The file opeation primitives are:

               1.  PRMClo
 - Closes an open RMS  file  and  returns  used
                   buffer space
 to the Pascal heap.

               2.  PrmCre - Creates an Rms File.   If  t
he  file  to  be
                   created is an indexed (ISAM) file, the PRMK
ey routine
                   must be called a minimum of one time  prior  to  
this
                   call.

               3.  PRMKey - Defines the keys o
f an indexed  file.   This



Pascal Record Management User's Manual           
               PAGE 1-4
Introduction to PRM


                   call  is us
ed prior to the PRMCre routine.  Each call
                   defines on key of
 the indexed  file.   Multiple  keys
                   must  be  defined in as
cending order.  In addition to
                   the RMSFileDesc buffer, a buf
fer of  TYPE  IdxKeyDesc
                   is also used with the PRMKey routin
e.

               4.  PRMOpe - Opens an existing RMS file


              
 PRM ensures that the user knows the file record  size  of
          the  file 
 specified for during PRMOpe.  The open requires the
          user to specify 
the record size of the file.   If  the  actual
          file  record  size  an
d  the user specified record size to not
          match, any activity on the f
ile is prohibited.

               PRM returns the standard RMS-11 Macro error
 codes.  



          1.4  Record Operations


               There are 
four record operation  primitives  provided  by
          the  PRM  interface. 
  An  address of buffer TYPE RetRecord is
          passed to PRMRet.  An addre
ss  of  buffer  TYPE  StoRecord  is
          passed to PRMSto for storing reco
rds.  The buffers contain the
          necessary parameters for access to the 
file.  

               Before the record  operations  are  performed,  PRM  w
ill
          check  to  see  if the file to be accessed is properly opened.
 
         Record operations performed on an improperly opened file  will
       
   produce  unpredictable  results.  Any record operation request
          per
formed on an RMS file that has not been successfully opened
          by PRMOpe
 will be rejected by PRMRet and PRMSto.

               The record operation p
rimitives are:

               1.  PRMDel - Delete the currently  selected  re
cord  from
                   the   file.    The   currently   selected  record
  is
                   established with a PRMRet call.

               2.  P
RMFre - Unlocks the bucket locked  by  the  previous
                   PRMRet 
 operation.   The bucket is locked only if the
                   file is opene
d with write access.

               3.  PRMRet - Retrieves a record from a fi
le  successfully
                   opened with PRMOpe.  A record is always pla
ced in the
                   RMS I/O internal buffer.  If a PGET type retrieva
l is
                   executed,  the  User Record Buffer (address passed by
                   the PRM user) is loaded.  If a PFIND  type  retrieval
      
             is executed, the user record buffer is not loaded.

             
  4.  PRMSto - Store or update a record  in  a  sucessfully



Pascal Record Ma
nagement User's Manual                          PAGE 1-5
Introduction to PRM




                   opened  file.   A  PPUT operation will generate a new
   
                record, a PUPDATE will update an existing record.




     
     1.5  RFA (Record File's Address)


               The PRM interface prov
ides access  to  file  records  via
          RFA's.   An  RFA is a unique numb
er assigned to each record of
          RMS type files.  The use of RFA provide
s direct  access  to  a
          record  by-passing  the record processing sof
tware.  Use of an
          RFA will also provide random access to  RMS  Sequen
tial  files
          that are stored on random access devices (disks).

    
           An example of RFA access usage would  be  an  application
          
that  searches  the file for records with specific conditions.
          The en
tire file is searched and  records  with  the  specified
          conditions a
re "remembered" for future reference.  

               When the entire file h
as been  searched,  the  processing
          begins  randomly accessing the fi
le for the specified records.
          If during the initial search, the RFA i
s stored, the  RFA  can
          be used to randomly access the record.  The s
toring of the RFA
          may be an alternative to storing the entire record 
(or key) in
          memory  for rapid access to the data after the initial se
arch.
          Storing the entire record (or key) may not be possible.

    
           The previous senario describes the use of DataTrieve when
          
forming a "collection".


                                       NOTE

    
          The RFA used to define a record is unique and  can  be
              
stored  in a file for access to records for subsequent
              executions
 of an application.   However,  the  RFA  is
              only  valid  for  th
e life of the file.  Once the file
              has been reorganized with a ut
ility such as CNV or IFL
              (or  an  application  program),  the  RF
A  for a given
              record is no longer valid.



               R
FA can be used to retrieve records only.  When you store
          a  new  reco
rd,  PRM  returns the RFA generated by RMS via the
          StoRecord buffer. 
 When you  retrieve  a  record  will  normal
          access, the record RFA i
s returned by PRMRet in the RetRecord.
          When you retrieve a record by 
RFA, you specify search  :=  RFA
          in  RetRecord  buffer  and load the 
RFA in KeyNum in RetRecord
          buffer.  The example in the appendix shows
  use  of  RFA's  to
          randomly retrieve records from a sequential file
.



Pascal Record Management User's Manual                          PAGE 1-6
Introduction to PRM


          1.6  Memory Requirements


               
PRM code requires approximately 1KW if all  routines  are
          used.   The
  space  used would be required by any interface to
          RMS-11 including 
MACRO-11 or any high level language.  PRM  is
          designed so only the re
quired calls are included.

               Dynamic memory space is managed by 
 the  Pascal  run-time
          system.  PRM defines a GSA routine (refer to p
aragraph 1.1) to
          efficiently control allocation and deallocation of P
ascal heap
          space.

               RMS-11 code  requires  approximat
ely  24KW  is  all  file
          organizations  with  all  RMS-11  file  and 
 record operations
          supported.  At present, PRM requests the task buil
der to  link
          ALL RMS-11 code to a PRM task.  If the RMS-11 Resident L
ibrary
          is not used, the user space remaining is serverly limited.  If

          not  using  RMS-11 Resident Library support, modify the RMSIni
    
      routine  and/or  use  DEC  supplied  ODL  (overlay  descriptor
          
language)  files.   Refer  to  paragraphs  2.5  and/or 2.6 for
          detail
.














                         CHAPTER 2

              
       Preparing for PRM




               The PRM User  Program  must  in
clude  the  PRM  interface
          structures  and  external procedure calls.
  All the structures
          and calls are provided as part of the PRM packag
e.   The  data
          structures   are  located  in  file  PrmPrefix.Pas.   
The  PRM
          Procedure calls are located in file PrmCalls.Pas.

       
        The following is an abbreviated list of  the  steps  that
          mus
t be followed to prepare your task for interface to PRM-11.
          Paragraph
s that follow detail each step.

               1.  Pre-Define  Data  Structur
es   -   Pre-defined   data
                   structures must be included in y
our source code.  The
                   data    structure     are     located 
    in     file
                   [300,47]PRMPrefix.Pas.

               2. 
 Control Buffers - Allocate  space  in  your  task  by
                   defin
ing  buffers  of  TYPES  defined  from  the data
                   structures 
 file.   The  buffers  are  used  to  pass
                   control  data  to
 PRM external routines.  Define only
                   the  buffers  required 
 to  satisfy   PRM   interface
                   requirements.

            
   3.  Record Buffers - Define data structures  to  describe
                  
 the  logical  record of your application.  An example
                   recor
d definition is included in the data  structures
                   file.    Al
locate  the  required  record  buffers  to
                   satisfy task requ
irements.

               4.  Key Buffers - Modify the KeyDef record definitio
n and
                   keysizes  in  CONST  to  describe  the  keys  of your


                   indexed and/or relative file(s).  Use variant records
     
              to  define  key(s)  of  the  RMS  file(s).   If  your
           
        application uses  RELATIVE  type  files,  define  one
                 
  entry  of  type  "TwoWord"  (defined in PRMPrefix) to
                   hold
 RELATIVE record numbers for retrieval and  store
                   operations
.  

               5.  External  Calls  -  Include  the  contents  of   file


                   PRMCalls.Pas.  Delete PRM procedure call(s) that will



Pa
scal Record Management User's Manual                          PAGE 2-2
Preparin
g for PRM


                   not be used.  This will avoid the  addition  o
f  code
                   that will not be used.

               6.  RMS-11 
Initialization - Modify  RMSIni  if  all  file
                   organizations
  and/or record operations are not used.
                   This is important  
if  not  using  the  RMS  Resident
                   Library.

             
  7.  Task Build - Reference object library  RMSPAS  during
                   
task build.  

               8.  User Space Optimization  -  Share  control  
and  data
                   buffers if space is limited.

               9. 
 PRM Pit-Falls - Check to  make  sure  your  task  has
                   speci
fied the proper parameters to PRM.




          2.1  Pre-defined Data Stru
ctures


               File PRMPrefix.Pas defines all  of  the  data  struct
ures
          that  are  used  to  pass user specified data to PRM routines.
          Data is transferred to external routines by passing an address
      
    reference  of  control  buffers  allocated in the main program
          sp
ace.  PRM routines expect a specific format  of  the  buffer
          therefor
e  PRM  external procedures and user programs must use
          formatted reco
rds.

               The buffer descriptions used  by  PRM  routines  and  PRM

          Users  are  not exactly alike.  For example, PRM routines full
    
      defined the RAB and FAB in the RMSFileDesc buffers.  The  user
          
RMSFileDesc  buffer  defines  the RAB and FAB as "work space".
          This d
ifference allows the user to ignore (and define)  fields
          within the R
AB and FAB.  The complexity of the user program is
          reduced because po
inter types in the RAB and FAB  are  defined
          externally  only.   Anot
her  difference  is the record and key
          buffer definitions.  PRM deter
mines the  size  by  using  size
          data  passed  by  the  user.  PRM ha
s to depend on the user to
          specify the proper sizes.



         
 2.2  Control buffers


               The control buffers provide the  user 
 with  a  means  of
          specifying  control  data  to PRM external routin
es.  PRM uses
          the control data loaded by the user to  load  the  RMS-
11  RAB
          (record  attributes  block)  and  FAB (file attributes block)
.
          Codes are generated by PRM to inidicate user  requests  passed



Pascal Record Management User's Manual                          PAGE 2-3
Prepar
ing for PRM


          via the control buffer fields.



          2.2.1
  RMSFileDesc - File Description


               The RMSFileDesc (RMS File  
Description)  type  buffer  is
          allocated  by the user in the main pro
gram space (heap space).
          A buffer is allocated for each simultaneousl
y open file (refer
          to  paragraph 2.2.9).  The buffer is loaded by the
 user before
          the PRMOpe (open file) procedure is called.  All procedi
ng PRM
          calls  pass  the  address of this buffer to the PRM routine to

          indicate the file to be used for the  record  operation.   The
    
      RMSFileDesc buffer provides PRM with space that is used as the
          
file RAB and FAB.  Since the buffer is allocated from the user
          space 
(versus locally), the contents of the RAB and FAB can be
          preserved be
tween PRM calls.



          2.2.2  RetRecord - Retrieval Record


     
          The RetRecord (Retrieval Record) type buffer defines  the
          u
ser retrieval parameters.  PRM also uses fileds in the buffer
          to pass
 back control data to the  calling  program.   The  PRM
          user  loads t
he buffer prior to each PRMRet (record retrieval)
          call.



      
    2.2.3  StoRecord - Storage Record


               The StoRecord (Store  
Record)  type  buffer  defines  the
          parameters  used  when  storing a
 record in an open file.  The
          buffer is used with PRMSto (store recor
d) external  procedure.



          2.2.4  IdxKeyDesc - Indexed Key Descrip
tion 


               The IdxKeyDesc (Indexed File Key Description) type buf
fer
          is  used  to  define  each key of a dynamically created RMS-11
 
         indexed file.  A buffer of this type is loaded prior to  using
       
   the PRMKey (key definition) external procedure.  



Pascal Record Managemen
t User's Manual                          PAGE 2-4
Preparing for PRM


      
    2.3  Record buffers


               The PRM user defines record  buffers
  to  hold  the  file
          logical  records.  One record buffer can be all
ocated for each
          file or record buffers can be  shared.   The  address
  of  the
          record  buffer  and size of the record buffer is passed to 
the
          PRMRet or PRMSto external procedures.  The external procedures
 
         use  the  size  and address of the buffer to load or store the
       
   data.  Size of the record buffer specified by the user  cannot
          be 
 checked  for accuracy by PRM external procedures.  If care
          the user 
specifies an incorrect buffer size, FATAL results can
          occur.  Refer t
o paragraph 2.2.9 for details.



          2.3.1  Non-shared record buffers



               If your program logic requires record data from more than
          one  file  simultaneously, serperate record buffers have to be
      
    allocated.  Buffers of the same type have to be  allocated  to
          sa
tisfy  Pascal  type checking.  The type checking if enforced
          when pas
sing the buffer to the external PRM procedures.

               Modify the Rec
Def buffer definition in  PRMPrefix.Pas  to
          safisfy  your  requiremen
ts.   Use  as  many  CASE  entries as
          required  to  specify  all  rec
ord  buffer  types.   If   your
          application  does  not  require the f
ile full record, allocate
          the size of the buffer required and indicat
e the size of  your
          buffer when you retrieve or store data by specify
ing a RecSize
          before the operation.

               In some cases, 
the record buffer size differences may  be
          significant.   Using  a  v
ariant  record definition may not be
          desirable due to allocation of t
he largest  variant  for  each
          buffer.   This  means that the smaller
 record buffer will have
          an unused space the size of the difference i
n size of the  two
          records.

               If the logical records 
of your application vary  in  size
          and  you  cannot  afford wasted sp
ace, define a sperate record
          TYPE for each record.  To safisfy Pascal
  TYPE  checking  when
          the  buffer  is  passed to external PRM proced
ures, define the
          PRMRet and/or PRMSto call(s) local to a user  proced
ure.   The
          locally  defined  procedure  call  will  be  the  same  as
 the
          globally defined call with the exception of  the  record  TYPE
          definition.  The external procedure call will be linked to the
      
    same PRM external procedure by the task builder.



Pascal Record Managemen
t User's Manual                          PAGE 2-5
Preparing for PRM


      
    2.3.2  Shared record buffers


               If your application does no
t require data from  different
          files  simultaneously,  the  same reco
rd buffer can be used to
          hold data from more than one file.  A record
 buffer address is
          passed  to  PRM  procedures  that  store  (PRMSto)
 or retrieve
          (PRMRet) records.  The record buffer used is determined 
by the
          calling program.



          2.4  Key Buffers


      
         Modify the KeyDef TYPE description to define the keys  of
          yo
u  file(s).   A  CASE  of all the TYPEs can be defined.  The
          RetRecor
d type buffer uses the KeyDef description to determine
          the key struct
ure.  Since the RetRecord places the KeyDef type
          field at the end of 
the RetRecord buffer, the key can  be  any
          size.  



          2
.5  PRM External Calls


               External   Procedure   calls   are   
defined   in    file
          PrmCalls.Pas.   Only the calls used in your appl
ication should
          be included in  your  source  code.   The  task  build
er  will
          include  the  PRM code form the PRM library for only the cal
ls
          referenced in the source.  Define the PRM procedures local  to
  
        user procedures if different record TYPE buffers are required.
        
  Refer to paragraph 2.3.1 for details.



          2.6  RMS-11 Initializat
ion


               There is only one initialization routine,  RMSIni.   Thi
s
          module  must  be  referenced  in  all tasks using PRM.  RMSIni
   
       defines a RMS-11 Macro that indicates to the task builder  the
         
 RMS-11  code  that  should  be  linked  to  the task.  The PRM
          packa
ge  assumes  worst  case  and  specifies  that  all  file
          organizatio
ns with support for all operations be included.

               If the user li
nks to the  RMS-11  Resident  library,  the
          support  of  one  or  all
  file  organizations  and operations
          requires the same amount of spa
ce (8KW, 2 APR's) from the user
          task.  If the RMS-11 Resident library
 is not supported on your
          system, the RMS-11 code would require  appr
oximately  24KW  of
          user space.



Pascal Record Management User's M
anual                          PAGE 2-6
Preparing for PRM


               I
f you DO NOT link to the RMS-11  Resident  library,  you
          should do th
e following:

               1.  Make your own copy of file RMSIni.Src to be  
used  by
                   your  task(s) with the same file access requirement
s.
                   Change  the  file  name  to  make  sure   your   task
  
                 references your copy of RMSIni.

               2.  Modify th
e entries following the $ORG  MACRO.   Refer
                   to  the  RMS-11
  Macro-11 Reference Manual, paragraph
                   1.1.2.  Specify only 
 the  file  organization(s)  and
                   file access operations requ
ired by your task.

               3.  Compile and assemble the modified modul
e.  

               4.  Reference the module in your source code.

        
       5.  Reference the modified module during the task build.


           
    In addition to indicating the code that is to  be  linked
          to the 
task, RMSIni also specifies a dynamic memory management
          routine.  The
 routine is defined  to  RMS-11  as  a  GSA  (Get
          Space) routine.

               It is essential that  RMSIni  be  located  in  the  .ROOT
      
    segement  of  an  overlayed  task.   The  routine  has  to  be
          av
ailable for RMS-11 at all times.  It is also essential  that
          the RMSI
ni routine be executed one time prior to any other PRM
          routines.  





          2.7  Task Building 


               When task building, the P
RMPAS.OLB must be referenced  in
          the  task builder command or overlay
 description file.  If you
          are using the RMS-11 Resident library, use
  the  DEC  supplied
          overlay  description  and  reference  RMSRES  wi
th  the RESLIB
          command file option.  If you are using overlays, selec
t on  of
          the standard DEC supplied overlay description files or use t
he
          DEC supplied command file MAKRMSODL.CMD to help tailor an  ODL
  
        file to fit your specific needs.  An example of an command and
        
  ODL file is provided in Appendix C.



          2.8  User Space Optimizat
ion


               If your application requires access to files that are no
t
          opened  simultaneously,  file  buffer  of TYPE RmsfileDesc can



Pascal Record Management User's Manual                          PAGE 2-7
Prepar
ing for PRM


          used for more than one file.  It is important that a 
 file  be
          closed  successfully  before  the  buffer  is used for anot
her
          file.

               In most cases, the RetRecord and StoRecor
d  TYPE  buffers
          can  be  shared  with  no  problems.   Only  when  i
t  is more
          efficient to maintain access  attributes  for  seperate  f
iles
          should seperate buffers be allocated.

               User rec
ord buffers can be shared  to  reduce  the  space
          used.   Paragraph 2
.3 details shared and non-shard user record
          buffers.  

           
    The  RMSIni  routine  should  be  modified  to  fit  your
          applica
tion   requirements.    Paragraph   2.5  describes  the
          modifications
 to RMSIni.



          2.9  PRM Pit-Falls


               PRM routines
 perform a certain amount of  error  checking
          to make certain that th
e PRM User follows RMS-11 and PRM usage
          guide lines.  There is howeve
r certain guide lines that cannot
          be checked because PRM routines are
 serperatly compilied.  PRM
          has to depend on the PRM user for items l
isted below.  If  the
          minimum  requirements  listed below are not met
, unpredictalbe
          error will result.



          2.9.1  Record Siz
e


               PRM routines depend on the PRM User to supply the  record


          buffer.   The  user  also  has to supply PRM routines with the
     
     size of the record buffer.  Since PRM routines  are  external,
          c
ompiled  seperately  and a general set of routines supporting
          any RMS
 file, there is no way that the routines can  accuratly
          check  buffer
  sizes  allocated  in the MAIN PRM User program.
          PRM depends on the 
PRM User to inform the external routines of
          the  size of the record t
o be retrieved or stored.  If the PRM
          User defines a record size that
  is  larger  than  the  record
          buffer  actually allocated, PRM (RMS)
 has to assume the record
          size is correct.  When a record is  retriev
ed  from  the  file
          user  code (or data) will be destroyed if the all
ocated buffer
          is smaller than the PRM User supplied record size.

 
              PRM  checks  the  user  record  size  specified  in   the
       
   RMSFileDesc  TYPE  buffer  when  the file is opened.  The user
          mus
t specify the exact file record size.  This  is  to  ensure
          that  the
  user  knows the characteristics of the file that is



Pascal Record Manageme
nt User's Manual                          PAGE 2-8
Preparing for PRM


     
     being opened.  A PRM error code will be returned if  the  file
          a
nd  user  declared record size do not match.  This however is
          only a 
check and does not ensure that user code  will  not  be
          destroyed.   
The  PRM  user should define a CONSTANT to define
          the size of the log
ical  record  buffer.   The  same  CONSTANT
          should  be  loaded  into 
 the  RMSFileDesc  buffer  before the
          PRMOpe.



          2.9.2 
 RMS Initialization


               If the RMSIni routine is not executed fi
rst in your task,
          unpredictable  results will occur.  RMS-11 assumes 
the the GSA
          routine (declared within  the  RMSIni  module)  is  const
antly
          available  for  use.   If  the GSA routine is not in the .ROOT


          segment of your task, RMS-11 will fail.   Refer  to  paragraph
     
     2.4   for  detailed  information  concerning  modification  of
          R
MSIni.



          2.9.3  File Sharing


               If the file be a
ccessed is to be used by  multiple  tasks
          simultaneously,  and  your 
tasks specifies write access to the
          file, the target bucket of a reco
rd  access  will  be  locked.
          When  a  bucket  is  locked,  the  reco
rds  in  the bucket are
          unaccessable  by  other  users.   When  your 
 application  has
          completed  the  access (or timed-out if waiting for
 an event),
          the bucket should be released by executing the PRMFre rou
tine.
          If your application specifies READ access to the file, buckets


          are never locked.














                         
CHAPTER 3

            Detailed Description of PRM Buffers




          
     This chapter gives detailed description of  all  the  PRM
          pre-de
fined   buffers  that  have  to  be  used  for  the  PRM
          interface.  
Brief descriptions of the fields  of  each  buffer
          are  provided.   D
etailed  description of data required by the
          field can be located in 
the RMS-11 User's Guide.



          3.1  RmsFileDesc - File Description




               The following describes the  fields  in  the  RMSFileDesc
   
       type buffer that are used to create an RMS file.  

               1.  
ORG - File Organization

                   1.  Description  :   The  file  or
ganization  of   an
                       existing  file  to  be  opened  or  
a  file to be
                       created.  Use one of the key word scalar t
ypes to
                       define  a  Sequential  (SEQ),  Relative  (REL) o
r
                       Indexed (IDX) file.

                   2.  Default 
:  None


               2.  FileName - File Name 

                   1.  
Description :  Full  file  specification  of  the
                       file  
being  created.   The file specification is
                       defined by t
he operating system being used.

                   2.  Default :  None


 
              3.  LogChan - Logical Channel Number 

                   1.  De
scription :  The logical channel number for the
                       file  I/
O  operations.  Refer to the task builder
                       manual options
 UNITS for details.



Pascal Record Management User's Manual                  
        PAGE 3-2
Detailed Description of PRM Buffers


                   2.
  Default :  None


               4.  Allow - System File Access

        
           1.  Description :  What other tasks can  do  to  this
              
         file  while  you have the file open.  If you want
                    
   exclusive access to the file specify NOSHARE.  If
                       you
  will  allow others to open the file, specify
                       SHARE.  I
f any other task has  previously  opened
                       the  file with 
NOSHARE, an error will be returned
                       when you attempt to o
pen the file.

                   2.  Default :  Share


               5. 
 Access - Program Access 

                   1.  Description :  Specifies wha
t the program opening
                       the  file can do while the file is
 open.  Specify
                       PREAD for read only, PWRITE for  write  
only  and
                       PBOTH for both ready and write access.  If PWR
ITE
                       or PBOTH is specified, target buckets are locked.
 
                      The  bucket  remains  locked until another target
       
                bucket is specified or the PRMFre call  is  used.
             
          If  the  file  is shared, bucket locking for long
                   
    periods of time should be avoided.

                   2.  Default :  Read
 Only


               6.  RecordSize - File Record Size 

                
   1.  Description :  The full size of the record of the
                      
 file  being  created  or  opened.  This should be
                       defin
ed as a Costant and also be used  to  define
                       the  size  
of the logical record buffer used.  If
                       an existing file 
is being opened, the exact  file
                       record  size  has  to b
e specified or a PRM error
                       code will be returned.

   
                2.  Default :  None 


               7.  DeferWrite - Deferr
ed Bucket Write to File

                   1.  Description :   Valid  for  in
dexed  files  only.
                       Normally  storage  of  each logical 
record causes
                       the contents of  the  entire  RMS  bucket 
 to  be
                       stored  in the file to ensure the contents of th
e
                       file  contains  the  most  up-to-date  data.   If
   
                    deferred  write  is selected, the bucket will not
         
              be written to the file until the bucket is full.



Pascal Record
 Management User's Manual                          PAGE 3-3
Detailed Descriptio
n of PRM Buffers


                   2.  Default :  No Deferred Write


 
              8.  Unlock - Unlock the file 

                   1.  Descriptio
n :  The file will not be locked  as  a
                       result of the im
proper closing of the file due to
                       program abort.  This s
hould not be used  for  RMS
                       Sequential files.

       
            2.  Default :  Lock the file if improperly closed


             
  9.  ObeyFill - Obey Bucket Fill Number

                   1.  Description :
  Each RMS bucket may  have  a  fill
                       number specified wh
en the file is created.  Since
                       the PRM user cannot speci
fy  the  value  of  this
                       parameter  during  PRMCre,  thi
s  feature is only
                       valid when opening an existing file c
reated  with
                       RMSDEF or RMSDFN.

                   2. 
 Default :  Fill the bucket as much as possible.


               10. MassIns
ert - Mass Insert records

                   1.  Description :  Used for RMS 
indexed  files  only.
                       Normally  RMS will traverse the in
dexed tree with
                       each record insert.  If this option is  
selected,
                       the  record  is placed in the file at the pres
ent
                       pointer  location.   Extreme  caution  should  be
 
                      exercised  when  using this option.  Refer to the
       
                RMS MACRO-11 Reference Manual for details.

                  
 2.  Default :  No mass insert


               11. FileEnd - File Pointer to
 End-Of-File

                   1.  Description  :   When  opening  an  exist
ing  RMS
                       Sequential  file  this  option  can be used.  T
he
                       option will position the file pointer to the  end
  
                     of  the  file  in preparation for the addition of
        
               records to the file.

                   2.  Default :  File po
inter to the beginning  of  the
                       file


              
 12. RecForm - Logical Record Format

                   1.  Description :  Th
e record format of fixed length,



Pascal Record Management User's Manual     
                     PAGE 3-4
Detailed Description of PRM Buffers


        
               variable   length   or   stream  format  records.
              
         Specify FFIX for a fixed length record, FVAR  for
                    
   a  variable length record and FSTREAM (sequential
                       fil
e only) for stream format.

                   2.  Default :  Fixed


     
          13. Allocation - File Block Initial Allocation

                   1
.  Description :  The number  of  disk  blocks  that
                       sho
uld  be initially allocated to the file during
                       file crea
tion.

                   2.  Default :  0 blocks


               14. Buck
etSize - RMS Bucket Size 

                   1.  Description :  A logical uni
t of storage for  RMS
                       files is known as the bucket.  Spe
cify the number
                       of blocks for each bucket.

          
         2.  Default :  1


               15. EXTQUA - Default File Extensio
n Quatity 

                   1.  Description  :   If  the  file   is   dynam
ically
                       extended,  this  number  specifies  the number of

                       blocks the file will be extended.  Should  always
    
                   be  specified  to  avoid  file header entries and
          
             hence file access performance degradation.

                   2.
  Default :  1 block extended


               16. Contiguous - Allocate the 
file in Contiguous Blocks

                   1.  Description :  The file  siz
e  specified  by  the
                       allocation  field  is allocated in
 contigous disk
                       blocks.   If  the  contigous   blocks   
are   not
                       available, an error is returned.  

        
           2.  Default :  Non-contiguous


               17. Temporary - Tem
porary File

                   1.  Description  :   The   file   will   be   
deleted
                       automatically  by  the  operating system when th
e
                       file is closed.  The file is  in  existence  only
   
                    while the file is open.



Pascal Record Management User's 
Manual                          PAGE 3-5
Detailed Description of PRM Buffers




                   2.  Default :  Permanent File





          3.2  Re
tRecord - Record Retrieval


               The following gives a description
 of the  fields  in  the
          PRM retrieval buffer RetRecord:

         
      1.  KEYNUM - Key Number

                   1.  General :  This value is
 usually  used  only  for
                       indexed  files  except  if  th
e access if by RFA.
                       The  field  is  not  used  if   the 
  fuke   file
                       organization is not an indexed file or the
 access
                       is not by RFA.

                   2.  Indexed
 Key :  If the Seach Type (defined  below)
                       is  EQ,  GT  
or GE then this entry is the Indexed
                       key number that RMS
 is to  use  for  data  record
                       retrieval.   This  number
  can be form 0 (primary
                       key) to n-1 where n is the numb
er of keys in  the
                       indexed file.

                   3
.  RFA :  If the Search Type (defined below) is  RFA
                       the
n  the Key Number is the RFA number.  Any file
                       organizat
ion  can  use  this  type   of   access.
                       Sequential  fil
es  can use random access if using
                       RFA access.  Refer to
 paragraph 1.4 for details.

                   4.  Default :  None


     
          2.  SEARCH - Mode of Record Search

                   1.  EQ, GT, G
E :  Search types of EQ, GT  or  GE  are
                       for access of I
ndexed records only.  These search
                       types  define   the  
 comparison   criteria   for
                       retrieving   records.   The
  comparison  is  made
                       between the data in the  KEYDATA 
 field  of  this
                       buffer  (defined  below)  and the conte
nts of the
                       file key data for the key specified in the KE
YNUM
                       (defined above) field.

                   2.  RF
A :  The RFA search type can be  for  any  file
                       organiza
tion.   The  KEYNUM  field must be loaded
                       with the RFA n
umber.

                   3.  NEX :  The NEX search type can be used to  acce
ss
                       the  NEXt  record in the file.  This mode is used





Pascal Record Management User's Manual                          PAGE 3-6
Detai
led Description of PRM Buffers


                       to sequential access 
records from a  Relative  or
                       Indexed file.  This is the 
only record access for
                       RMS Sequential files.  This mode 
 is  used  after
                       positioning  the record stream to a fil
e position
                       using a random access search.  The random  ac
cess
                       search is executed using PrmRet witha GET or FIND
                       operation.

                   4.  REC :  The REC searc
h  type  specifies  that  the
                       KEYDATA  field  (described
  below)  is  a  record
                       number of a Relative file type.




               3.  RECSIZE - Logical Record Size 

                   1. 
 Input :  You must specify the size of the  record
                       you  
 want   retrieved   prior   to  each  PrmRet
                       operation. 
 Since the field is both an input  and
                       output,  the reco
rd size loaded will be destroyed
                       and therefore  must  be
  reloaded.   This  is  an
                       effort  by  PRM  to  make sur
e the user knows the
                       record size.

                   
         RMS will transfer all or part of the  record
                       fr
om  the  file.   If  you specify recsize < file
                       record s
ize, only part  of  the  record  will  be
                       transferred  a
nd  the  RMS  error  ERRTB  will be
                       returned.  If you sp
ecify recsize >  file  record
                       size,  the record buffer w
ill be partially filled
                       with the record and PRM will  lo
ad  RECSIZE  with
                       the size of the record transferred to 
your record
                       buffer.

                            If yo
u specify a  record  size  >  than  the
                       allocated buffer
, PRM will assume the record size
                       to be correct.   The  
record  will  destroy  data
                       following  the record buffer
.  Refer to paragraph
                       2.9 for details.

              
     2.  Output :  The size of the record  retrieved  from
                    
   the  RMS  file is loaded in this field and passed
                       bac
k to the calling program.  This may be  useful
                       informati
on  when  variable  length  records  are
                       used.


    
           4.  RFAOut - RFA output from PRM

                   1.  Descriptio
n :  The  RFA  (Records  File  Address)
                       generated  by  R
MS, unique for each record in the
                       file is available to t
he  calling  program.   For
                       details refer to paragraph 1
.4.  




Pascal Record Management User's Manual                          PAGE
 3-7
Detailed Description of PRM Buffers


               5.  KEYSIZE - Size
 of the key data

                   1.  Description :  Valid for indexed file
s only.   If
                       you  want  a  generic  search, specify the 
search
                       type of EQ, GT or GE then specify a key size that

                       is  <  the  full key size of the specified key in
    
                   KEYNUM.  For example, if the key data is for  zip
          
             codes  and  you  want  all records with zip codes
                
       that begin with 5501,  load  KEYDATA  with  5501,
                      
 search=EQ,  KEYSIZE=4,  execute  a PRMRet and the
                       first
 record in  the  file  with  5501x  will  be
                       returned.  
Switch to sequential access (NEX seach
                       type) and call PR
MRet to access all  the  records
                       within the generic zip 
code range.

                   2.  Default :  None


               6.  KE
YDATA - String or Integer key data

                   1.  Indexed :  The stri
ng or integer value the PRMRet
                       operation  is  seaching  
for in the indexed file.
                       RMS will search the file for a 
key  according  to
                       the  search  mode  specified  in the 
Search field
                       (above).

                   2.  Relative
 :  The relative record number of  a  RMS
                       relative file.






          3.3  StoRecord - Record Storage


               The  s
torage  type  operations  use  the  StoRecord  type
          buffer.  The foll
owing describes the StoRecord fields:

               1.  RecSize - Record Siz
e

                   1.  Description :  The size of the  data  record  you
 
                      want  stored  in the RMS file.  You can specify a
       
                record size <= to full record size for files with
             
          variable record formats.  If you specify a record
                   
    size > the allocated record buffer, data that  is
                       no
t part of the logical record (garbage following
                       the reco
rd buffer) will be assumed as part of the
                       record.    The
   record   in  the  file  will  be
                       corrupted.

      
             2.  Default :  None




Pascal Record Management User's Manual   
                       PAGE 3-8
Detailed Description of PRM Buffers


      
         2.  RFAOut - The RFA generated by RMS-11 when the  record
            
       was  stored  in  the  file.   The  RFA  can be stored
                  
 internally if the record is to be accessed at a later
                   withi
n the same application.

               3.  KEY - RELATIVE Files only, The rel
ative record number
                   of the target cell for the record to be 
stored.




          3.4  IdxKeyDesc - Indexed Key Description


      
         This buffer is used to define the keys of  a  dynamically
          cr
eated indexed file.  The buffer is loaded and PRMKey routine
          is calle
d to describe each key of the file being created.  The
          keys must be d
efined in ascending order.

               The following describes the fields 
 of  the  record  type
          IdxKeyDesc:

               1.  KeyNum - Ind
exed Key Number

                   1.  Description :  The indexed key  number
  that  the
                       record  describes.   This  can be any number
 from
                       0-255.  

                   2.  Default :  None



               2.  KeyPos - Key Position in the Record

                
   1.  Description :  The starting byte position  (start
                      
 with 0) of the key in the logical record.

                   2.  Default :  
None


               3.  KeySiz - Size of the Key

                   1.  
Description :  Size in bytes of the key defined.

                   2.  Defau
lt :  None


               4.  KeyTyp - Key Type

                   1.  D
escription :  The key can be of type  string  or
                       integer
.   Other  types of keys are available but
                       not supported
 by PRM.

                   2.  Default :  String



Pascal Record Managemen
t User's Manual                          PAGE 3-9
Detailed Description of PRM B
uffers




               5.  KEYDUP - Duplicate Key

                   
1.  Description :  If the key  being  defined  allows
                       du
plicate entries, specify a "Y" in this field.

                   2.  Default 
:  No Duplicates


               6.  KEYCHG - Key value change 

         
          1.  Description :  Valid for alternate keys only.  If
               
        selected the value of the key may be altered on a
                     
  record update.  

                   2.  Default :  No Changes


        
       7.  KeyNul - Key Null value

                   1.  Description :  Vali
d for alternate keys only.  If
                       a  keyed field of the rec
ord is not valid for all
                       records in the file, a  null  k
ey  value  can  be
                       specified.   If  a  null key value is
 defined and
                       the field if  FILLED  with  the  null  key 
 value
                       during  a record insert (PRMSto - PUT) there will

                       be no  entry  in  the  alternate  key  structure.
    
                   Example:   Key  in an employees record describing
          
             the name of the company softball  ball  team  the
                
       employee  belongs to.  A null key value should be
                      
 specified so unneccessary  entries  in  the  tree
                       struc
ture  for  the alternate key are not entered
                       for employe
es that are not on any softball team.

                   2.  Default :  No Nu
ll





          3.5  User Defined Record Buffers


               The
 RecDef Record TYPE has to be modified to  define  the
          fields  of  yo
ur logical record.  Multiple CASE entries can be
          used to define all t
he logical records.  Once  the  buffer  is
          defined, one or more recor
d buffers should be allocated in the
          user space.  Refer to paragraph 
2.3 for more detail.














                         CHAPTER 
4

            Detailed Description of PRM Routines




               Th
is chapter describes the PRM calls  used  to  interpret
          the User's re
quest and pass the request to RMS-11.



          4.1  General Use


   
            To use any of the  PRM  calls,  the  user  must  properly
         
 prepare  the  task  with  the proper buffer types and external
          calls
.  The following list the coding rules to follow for  PRM
          calls:

 
              1.  The RMSIni routine must be executed before any  other
       
            PRM routine is called.

               2.  The calling routines mu
st be  OMSI  Pascal  V1  only.
                   Pascal V2 main program routin
es will not work for the
                   present version of PRM.  Pascal V1.
2H  code  has  not
                   been  tested.   If  used, specify the con
tents of all
                   fields rather than taking the defaults.

    
           3.  Once a file has  been  opened,  file  work  space  is
          
         allocated  in  the  buffer  of  TYPE  RmsFileDesc you
                
   provide on the open.  This buffer  is  used  for  all
                   fil
e operations on that file.

               4.  A variable of TYPE RMSStatus wo
rd should  be  checked
                   after  ALL PRM calls.  The value of +
1 will inidicate
                   success, a negative value will indicate fai
lure.  

                        The negative value can be a PRM error or an  
RMS
                   type  error.   If  an RMS error, word 1 of the status
 
                  will be loaded with the RMS STS and word 2  with  the
       
            RMS  STV  value.   Definition  of these errors can be
             
      found in the RMS User or RMS Macro Reference Manuals.
                   
The PRM returned error codes are defined in the CONST
                   sectio
n of [300,47]PRMPrefix.Pas and Appendix D.



Pascal Record Management User's M
anual                          PAGE 4-2
Detailed Description of PRM Routines




               5.  Do not perform any record operations unless the  file
   
                has  been  properly  opened  and initialized.  If PRM
         
          routines (PRMOpe or PRMCre) do not successfully  open
               
    the  RMS  file  all  PRM  record  operations  will be
                   in
hibited and error code PrIni will  be  returned  in
                   word 1 o
f the status.  If PRM allow record operations
                   on a inproperl
y opened  file,  unpredictable  results
                   could occur.

    
           6.  If the RmsFileDesc buffer is used for multiple files,
          
         care  must  be  used.   When  using  the  buffer  for
                
   multiple files, be sure  to  close  the  file  before
                   re-
use then reload the buffer with the new parameters
                   describin
g the file.




          4.2  File Access and Creation


              
 The following paragraphs describe the PRM  routines  that
          are used t
o access or create RMS-11 files.  All file types are
          supported for bo
th the access to existing files  and  creation
          of  new  files.   The 
following describes the requirements for
          the use of each file  type  
external  procedure  and  possible
          errors that can occur from their u
se.



          4.2.1  PrmClo 


               This procedure is used t
o close an open  RMS  file.   The
          RMSFileDesc type buffer passed to t
he procedure inidicates the
          file to be closed.  The RMS Sts  and  Stv
  values  are  passed
          backed to the calling program.  These values sh
ould be checked
          to ensure the close was successful.



          
4.2.2  PrmCre


               This procedure is used to dynamically create a
n RMS file.
          All  file  organizations can be created by simply definin
g the
          file type you want created  and  loading  the  remaining  file


          creation fields in the RMSFileDesc record.  Before calling the
     
     PRMCre routine, the PRMKey routine must be called at least one
          t
ime.



Pascal Record Management User's Manual                          PAGE 4-
3
Detailed Description of PRM Routines


          4.2.3  PrmKey


      
         This call is used  when  you  desire  to  create  an  RMS
          in
dexed  file.   Call PrmKey to define each key of the indexed
          file pri
or to the PrmCre call.  PrmKey can be called  multiple
          times defining
 a new key with each call.  The keys are defined
          in a buffer of type 
IdxKeyDesc.  When defining more  than  one
          key,  define  the  keys  i
n  ascending order starting with the
          primary key (key 0).  RMS will g
enerate an error on the create
          if you do not follow this convention.





          4.2.4  PrmOpe 


               This procedure will open an 
exising RMS type  file.   The
          file  can be previously defined with an
 RMS utility (RMSDef or
          RMSDfn) or by any other program that has  cre
ated  the  RMS-11
          file.

               When the file is opened,  P
RM  FATAL  conditions  may  be
          detected.   The  error  is  the  resul
t  of  not following PRM
          conventions.  The error code is returned in 
the PrmStatus.   A
          description  of  these error codes is described in
 Appendix D.
          These type of errors should be corrected immediately.



               If  PrmOpe  does  not  properly  initialize,  ALL  record
     
     operations  on  the  file  will  be  rejected  by  PRM  record
          o
perations.  This feature is for the  user  that  ignores  the
          error c
odes returned from PrmOpe.  If the file is not properly
          opened and re
cord operations are performed, the task may abort
          with  ODD  ADDRESS 
(or other) type fatal errors.  A recordsize
          specified in the RmsFileD
esc buffer <>  file  record  size  is
          considered improper initializat
ion.



          4.3  Record Access and Storage




          4.3.1  P
rmDel 


               This procedure is used  to  delete  a  record  previo
usly
          located with a SUCCESSFUL PrmRet PGET or PFIND operation.  The
          user should make  sure  that  the  file  pointer  is  properly
      
    positioned  before  calling this procedure.  That is, the user
          mu
st  check  the  PrmStatus  code  returned  from  the  PrmRet
          operatio
n for a success code (+1) before calling PrmDel.



Pascal Record Management Us
er's Manual                          PAGE 4-4
Detailed Description of PRM Routi
nes


          4.3.2  PrmFre 


               This procedure is used to 
unlock a bucket so other  tasks
          can  access records in the bucekt.  B
uckets are locked only if
          the file is opened with ACCESS of PWRITE or
 PBOTH.  The Access
          field  default  of  Read  only  should  be  selec
ted  if  your
          application is only going to read data.  This access wi
ll  not
          lock  buckets  and  therefore this call would never have to b
e
          used.  

               If you specify a write  or  read/write  a
ccess,  the  RMS
          bucket will be locked when you access records in the
 bucket of
          the file.  The lock will remain on the bucket  until  1)  
your
          application  accesses  another  record  not  in  the presently
          locked bucket, 2) your application closes the file or 3)  your
      
    application executes the PrmFre call.

               If your application 
is updating or writing records  in  a
          shared  file,  this  call shoul
d be kept in mind.  The call is
          especially useful when dealing with i
nteractive type programs.
          The  operator  response  should be timed if
 the application is
          holding a bucket locked and the continutation of 
 the  program
          is  dependant  on  the  operator  (who may have just go
ne on a
          coffee break).



          4.3.3  PrmRet 


         
      This call is used to retrieve a record  from  a  properly
          opene
d  RMS file.  Before access to the RMS file is attempted,
          a check is 
made to see if  PrmOpe  has  been  called  and  has
          properly  opened 
 the  file.   If the file has not been opened
          properly, a FATAL messa
ge  will  be  printed  and  the  RMSRet
          operation will not be perform
ed.

               Load the RetRecord buffer prior to using this call.  With


          the  call, specify a PGET or PFIND record operation.  Refer to
     
     the RMS-11 User's Guide for detail  concerning  GET  and  FIND
          r
ecord operations.



          4.3.4  PrmSto 


               This proce
dure is used to store a record in a  file  that
          has  been  properly  
opened with PrmOpe or PrmCre.  The PrmSto
          Call defines the type of op
eration with the  first  parameter.
          If the PrmSto describes an PUPDAT
E, the store must be preceded
          by a successful  PRMRet  operation.   I
f  you  define  a  PPUT



Pascal Record Management User's Manual              
            PAGE 4-5
Detailed Description of PRM Routines


          operat
ion,  the  record in stored in a new location in the RMS
          file.  Refer
 to the RMS-11 User's Guide for detail  concerning
          the PUT and UPDATE
 record opeations.














                         APPENDIX A


       PRM Program Example - Access to existing files



 
PROGRAM PrmE
xample ;
 
CONST
  IdxLch	= 3 ;		{ of the first 6 UNITS } 
  RelLch	= 4 ;		{
 ch. 3  4 avail. by default }
  SeqLch	= 7 ;		{ must spec. UNITS=n for units > 
6 }
 
  ExaRecSize	= 28 ;		{ full record size }
 
  { example labels and siz
es follow - user defines buffer sizes and labels }
  Key0Size	= 4 ;		{ user def
ines size of largest key }
  Key1Size	= 3 ;		{ user defines these labels and si
zes }  
 
 
TYPE
  RecDef1 	= RECORD	{ user defined record type  1 }
    Se
cNum	: ARRAY [1..4] OF CHAR ;	{ section number }
    SecSup	: ARRAY [1..3] OF C
HAR ;	{ sup initials }
    Fill	: char ;
    SecDesc	: ARRAY [1..20] OF CHAR 


    END ; { RECORD }
 
  RecDef2	= RECORD	
    EmpNum	: ARRAY [1..6] OF CHAR
 ;
    EmpName	: ARRAY [1..30] OF CHAR ;
    END ; { RECORD }
 
  KeyDef	= R
ECORD
    CASE integer OF	{ user defines keylabels and sizes, as many as req. }

      1 : ( Idx0 : ARRAY [1..Key0Size] OF CHAR) ; { index file prim. key 0 }
      2 : ( Idx1 : ARRAY [1..Key1Size] OF CHAR) ; { index file alt key 1 }
    
  3 : ( RecNum : TwoWord ) ;  { REL file rec.  , Org=REL, Search=REC }
    END 
;
 
 
{**********************************************************************
*
                     BEGIN PRM CONST and TYPE
        FILE [300,47]PrmPrefix
.Pas
          Refer to file [300,47]PrmCalls.Pas for Procedure Calls 



PRM 
Program Example - Access to existing files                          PAGE A-2



 *********************************************************************** 
M
aintainer: KGT
Version 1.3
 
}
  
CONST
  { * Error values returned in sta
tus word 1 and word 2 with each PRM call.
    * All errors set Status[1] to a n
egative value.
 
    *** ALL PRM CALLS SHOULD CHECK FOR A STATUS[1] RETURN VAL
UE OF < 1.
 
    * All DEC Rms errors are between -1 and -2000 decimal.
    *
 All PRM errors are between -5000 and -5100 decimal.  
 
  Symbolic  Status[1]
  Status[2]  Description      
									}
  PrINI	= -5001 ;    { NA       A re
cord operation was attempted on a file
 				that was not properly opened by Prm
Ope or
				PrmKey.  Check proper open or create of
 				a file before continui
ng with record ops. 
				}
  PrRNE	= -5002 ;  { Lch  	An existing file was ope
ned and the user
				program did not specify the correct file
				max. record 
size.  The logical channel no.
				of the file attempting to open is in word 2.

				All record operations will be inhibited.
				Use rms utility RMSDSP to de
termine actual
				record size and correct user recordsize.
				}
  PrRsz	= -
5003 ;  { RecSz	During a PrmRet call a record size must be
				specified so Prm
 knows the size of the 
				record to be returned.  The record size
				field 
is an input and output field therefore
				is must be loaded before EACH PrmRet
.  A	
				PrmRet rms failure will set the record size
				field to 0.  
				T
he record size specified by the user is
				returned in word 2.
				}
  PrKY0
	= -5004 ;   { NA	During a PrmKey call the primary key must
				be specified fi
rst.  
				}
  PrKNS	= -5005 ;   { NA	During a PrmCre call a indexed file 
		
		organization was specified and no primary key
				defined.  You must use PrmK
ey to define at
				least a primary key for indexed files.
				}
  PrAsc	= -5
006 ;   { NA	Keys defined to PrmKey were defined in a
				non-ascending key ord
er.  
				}
 
  {Erxxx    STS        STV      Rms error sts and stv error val
ues are 



PRM Program Example - Access to existing files                     
     PAGE A-3



  				returned for all rms errors.  The same 
   				symbo
lic values used by DEC (without $)
				are used to describe the errors.  Not al
l
				rms error codes are provided but may be
 				added.  Refer to index of R
ms User Ref.  
				}
  ErDup	= -544 ;		{ insert duplicate rec with no dups all
owed }
  ErEof = -592 ;		{ record processing reached end-of-file }
  ErFac = -
656 ;		{ record opr does not match declared access }
  ErFnf = -736 ;		{ file n
ot found during open }
  ErRlk = -1440 ;		{ target record was locked by another
 task }
  ErRnf = -1472 ;		{ random get or find did not locate record }
 
 
 
  NameSize	= 30 ;		{ sz of RMS input file name, do not alter }
 
 
TYPE
 
 TwoWord	= ARRAY [1..2] OF integer ;	{ record number size }
 
 
{ Following R
ecDef and KeyDef RECORDS are EXAMPLES only -
        define similiar RECORDS in
 MAIN Program TYPE specifications 
  RecDef = RECORD	 user defines field names 
and sizes 
    CASE integer OF	
      1 : (FXDat1 : ARRAY [1..10] OF CHAR ;
 
          FXDat2 : integer ) ;
      2 : (FYItem1 : ARRAY [1..30] OF CHAR ;
  
         FYItem2 : REAL ) ;
    END ;
  KeyDef = RECORD
    CASE integer OF  
  " user defines keylabels and sizes, as many as req. "
      1 : ( KeyX : ARRA
Y [1..10] OF CHAR) ;
      2 : ( KeyY : ARRAY [1..12] OF CHAR) ;
      3 : ( R
Num : TwoWord ) ;   " use this def. of relative rec.   if req. "
    END ;
}
 
  RmsFileName	= ARRAY [1..NameSize] OF CHAR ;	{ file name, do not alter }
  
RmsStatus	= ARRAY [1..2] OF integer ;	{ returned rms status codes }
 
  {    T
he following record holds the file being descibed with options
   selected by t
he user.  Space for this buffer is allocated in the user
   area.  Rab and Fab 
for the file is allocated within this buffer.  The
   address of this buffer is
 initially passed to Open then passed with 
   all record operations (get, put,
 update, delete, find and close) so 
   the routines know what file the operati
on is being performed on.
  }
  OrgTypes	= (SEQ,REL,IDX) ;	{ block i/o not sup
ported }
  AllowTypes	= (Share,NoShare) ;      { what others can do }
  Access
Types	= (PRead,PWrite,PBoth) ; { what you can do to the file }
  FormType = (FF
IX,FVAR,FSTREAM) ;	{ record format type }



PRM Program Example - Access to ex
isting files                          PAGE A-4



 
  { iF FIELD NOT ALTERE
D, DEFAULT WILL BE SELECTED }
  RmsFileDesc	= RECORD
    { -- Use with PRMOPE 
-- }
    Org		: OrgTypes ;	{ spec. file type, no SEQ }
    FileName	: RmsFileN
ame ;	{ full spec. of rms file, NO DEFAULT }
    LogChan	: integer ;	{ spec. ch
. n, NO DEF., n<= TKB UNITS=n }
    Allow	: AllowTypes ;	{ what others may do w
ith file, DEF Share }
    Access	: AccessTypes ;	{ what you may do to the file,
 DEFAULT Read }
    RecordSize  : INTEGER ;	{ MUST = max. file rec. size, NO DE
FAULT }
    Windows	: INTEGER ;	{ no. of ret. windows, DEFAULT usually 7 }
 
    { enable the following options with a capital "Y", ANY OTHER = DEFAULT }
  
  DeferWrite	: CHAR ;	{ IDX, defer write, def. write each record }
    Unlock  
  	: CHAR ;  	{ REL  IDX, don't lock if abort, DEF. LOCK }
    ObeyFill	: CHAR 
;	{ obey bucket fill numbers, DEF. FILL TO MAX }
    MassInsert	: CHAR ;	{ IDX,
 ref. rms-11 macro ref. man. rab rop }
    FileEnd	: CHAR ;	{ SEQ only, place f
ile stream at end of file }
 
    { file creation fields }
    RecForm	: Form
Type ;	{ rec. format, FSTREAM for seq., Def.= FFix }
    Allocation  : TwoWord 
;	{ no. blocks allocated to file, DEF. 0 BLKS }
    BucketSize	: integer ;	{ da
ta bucket size, DEFAULT BUCKETSIZE = 1 }
    ExtQua	: integer ;	{ no. blks dyna
mic extend file, DEFAULT 1}
    { Enable following with capital "Y", if not loa
ded, default is selected }
    Contiguous	: CHAR ;	{ create a contiguous file, 
DEF. FRAGMENTED }
    Temporary	: char ;	{ delete the file when closed, DEF. NO
 DEL. }
 
    WorkSpace	: PACKED ARRAY [1..160] OF char ;
  END ;	{ RmsFileDe
sc Record }
 
  SearchTypes	= (EQ,GT,GE,RFA,NEX,REC) ; { for GET use KeyData(E
Q'=',GT'>',
                    GE'>='), RFA, next seq. rec(NEX) or Rec.   (org
=REL) }
  ThreeWord	= ARRAY [1..3] OF Integer ;	{ for RFA's, big file huh }
  
RecOps	= (PGET,PFIND,PPUT,PUPDATE) ; { PRM record operations }
  RetRecord = RE
CORD
    { - USE with PRMRET, INPUT - to GET and FIND - INPUT/OUTPUT ref. to PR
M }
    KeyNum	: Threeword ;	{ INPUT- IDX Key   or RFA, search defines }
    S
earch	: SearchTypes ;	{ INPUT - spec. search opr }
    RecSize	: integer ;	{ IN
PUT - sz rec. to GET, (sz of rec. buffer)
                                  OUT
PUT- sz rec. returned to user rec. buf }
    RFAout	: ThreeWord ;	{ OUTPUT- val
id if search <> RFA }
    KeySize	: integer ;	{ INPUT - size of key data, <= fu
ll key size }
    KeyData	: KeyDef ;	{ INPUT - IDX or REL, key string or rec.  
 }
  END ;	{ RetRecord RECORD Definition }
 
  StoRecord = RECORD
      { US
E with PRMSTO, Input to PUT and UPDATE - INPUT/OUTPUT ref. to PRM }
      RecSi
ze	: integer ;	{ INPUT - spec. part or all or rec. buffer 
                    
              data to be stored, <= full rec. sz }
      RFAOut	: ThreeWord ;	{
 OUTPUT - rfa where record was stored }
      Key	: KeyDef ;	{ INPUT - REL ONLY
, spec. rec.   for store }
    END ;	{ StoRecord Record }



PRM Program Examp
le - Access to existing files                          PAGE A-5



 
  KTyp
e = (StrKey,IntKey) ;	{ string or unsigned integer key type }
  { Use with MULT
IPLE calls of PRMKEY to define ALL keys of an indexed file. 
    MUST be used a
t least once prior to PrmCre of an indexed file type }
  IdxKeyDesc = RECORD
 
     KeyNum	: Integer ;	{ key of ref.  , def. asc. order, start 0 }
      KeyPo
s	: Integer ;	{ byte position of key in rec., start byte 0 }
      KeySiz	: Int
eger ;	{ size of the key defining, max. = 255 }
      KeyTyp	: KType ;	{ string
 or unsigned integer, def.=string }
      KeyDup	: char ;	{ 'Y' to allow duplic
ate keys, def. no dup }
      KeyChg	: char ;	{ 'Y' for key changes, alt. only,
 def no chg }
      KeyNul	: char ;	{ null key value, alt. string keys only }
    END ;	{ IdxKeyDesc }
 
 
  {*********************************************
**************************
 *                   END PRM CONST and TYPE         
                   *
 *********************************************************
************** }
  
  
 
 
VAR
  chtfile	: text ;
  Rlen		: integer ;
  
i		: integer ;
  SeqRfas	: ARRAY [1..4] OF ThreeWord;	{ used to store rfa's }
 
  IdxFile	: RmsFileDesc ;	{ file parameters for idx file }
  IdxStoBuf	: Sto
Record ;	{ store buffer, shared by rel file }
 
  RelFile	: RmsFileDesc ;	{ fi
le parameters for rel file }
 
  SeqFile	: RmsFileDesc ;	{ file parameters for
 seq. file }
  SeqStoBuf	: StoRecord ;	{ store buffer for sequential file }
 


  RecBuf	: RecDef1 ;	{ same record buffer for all files }
  RetBuf	: RetRecord
 ;	{ retreival buffer, same for all file }
  RfaBuf	: Threeword ;	{ returned rf
a from record ops }
  Status	: RmsStatus ;	{ returned rms status codes }
 
 


{ ********** INCLUDE ONLY PRM CALLS REQUIRED ********** }
 
{ close the file 
}
PROCEDURE PRMClo ( VAR Filebuf : RmsFileDesc ;	{ ref. to file to close }
   
                VAR Status  : RmsStatus ) ;	{ STS and STV }
                   
EXTERNAL ;
 
{ Delete a record, must be preceded with successful GET or FIND (
PRMRet) }
PROCEDURE PRMDel ( VAR FileBuf : RmsFileDesc ;	{ ref. to file to dele
te rec }
                   VAR Status  : RmsStatus ) ;	{ STS and STV }
      
             EXTERNAL ;



PRM Program Example - Access to existing files      
                    PAGE A-6



 
{ Open an RMS Indexed file previously def
ined with RMSDEF }
PROCEDURE PRMOpe ( VAR FileBuf : RmsFileDesc ;   { load fiel
ds before open }
                   VAR Status  : RmsStatus ) ;	{ status of Sts
 and Stv }
                   EXTERNAL ;
 
{ Record retrieval from the specif
ied file }
PROCEDURE PRMRet( Operation : RecOps ;		{ define GET or FIND }
    
               VAR FileBuf : RmsFileDesc ;	{ ref. to file for access }
        
           VAR RetData : RetRecord ;	{ load with type of opr }
                
   VAR RecBuf  : RecDef1  ;	{ rec. buf connected to use }
                   VA
R Status  : RmsStatus ) ;	{ status of STS and STV }
                   EXTERNAL
 ;
 
{ Store a record in the specified file }
PROCEDURE PRMSto ( Operation   
: RecOps ;	{ define PUT or UPDATE }
                   VAR FileBuf : RmsFileDes
c ;	{ ref. to file for store }
                   VAR StoData : StoRecord ;	{ s
tore variables }
                   VAR RecBuf  : RecDef1  ;	{ rec. buf connect
ed to use }
                   VAR Status  : RmsStatus);	{ STS and STV }
     
              EXTERNAL ;
 
{ Define a routine to GET and DISPOSE heap space, e
xecute first in root seg }
PROCEDURE RMSIni ; EXTERNAL ;
 
 
PROCEDURE OpenF
iles ;
BEGIN
 
{ open an rms indexed file }
WITH IdxFile DO
  BEGIN
    Or
g := IDX ;			{ file orgainization code }
    FileName :=   '[300,47]PrmExa.Idx 
           ' ; { file name }
    LogChan := IdxLch ;			{ file logical channel n
umber }
    Access := PBoth ;			{ both read and write to the file }
    Record
Size := ExaRecSize ;		{ get full record }
  END ;
{ all fields not specified w
ill take their default condition }
PrmOpe ( IdxFile, Status ) ;
IF Status[1] <
 1 THEN writeln('Idx Open error, code=',Status[1], Status[2] ) ;
 
{ open and 
rms relative file }
WITH RelFile DO
  BEGIN
    Org := REL ;
    FileName :=
   '[300,47]PrmExa.Rel            ' ;
    LogChan := RelLch ;
    Access := PB
oth ;			{ both read and write to the file }
    RecordSize := ExaRecSize ;
  E
ND ;
PrmOpe ( RelFile, Status ) ;
IF Status[1] < 1 THEN writeln('Rel Open erro
r, code=',Status[1], Status[2] ) ;



PRM Program Example - Access to existing 
files                          PAGE A-7



 
{ open an rms sequential file 
}
WITH SeqFile DO
  BEGIN
    Org := SEQ ;
    FileName := '[300,47]PrmExa.S
eq            ' ;
    LogChan := SeqLch ;
    Access := PBoth ;			{ both read 
and write to the file }
    SeqFile.FileEnd := 'Y' ;		{ pointer to end of file 
for PrmSto }
    RecordSize := ExaRecSize ;
  END ;
PrmOpe ( SeqFile, Status 
) ;
IF Status[1] < 1 THEN writeln('Seq Open error, code=',Status[1], Status[2] 
) ;
 
END ;	{ PROCEDURE Openfiles }
 
 
PROCEDURE AddNewRec ( VAR TarFile :
 RmsFileDesc ; 
                      VAR TarRec : RecDef1 ;
                 
     VAR TarStoBuf : StoRecord ) ;
  PROCEDURE StoreIt ;
  BEGIN
    TarStoBu
f.RecSize := ExaRecSize ;	{ specify each time }    
    PRMSto ( PUT, TarFile, 
TarStoBuf, RecBuf, Status ) ;
    writeln('store ', status[1],status[2]);
  EN
D ;
 
BEGIN
  TarStoBuf.RecSize := ExaRecSize ;	{ spec. record size to store 
}
 
  { load the record buffer }
  TarRec.SecNum := '86A ' ;
  TarRec.SecSup
 := 'AAC' ;
  TarRec.SecDesc := 'some computer nurds ' ;                   
  
StoreIt ;
 
  TarRec.SecNum := '86C ' ;
  TarRec.SecSup := 'TMT' ; 
  TarRec
.SecDesc := 'ALL computer nurds  ' ;
  StoreIt ;
 
  TarRec.SecNum := '86B ' 
;
  TarRec.SecSup := 'WHO' ;
  TarRec.SecDesc := 'more computer nurds ' ;
  S
toreIt ;
 
END ;	{ PROCEDURE AddNewRec }
 
PROCEDURE XferToSeq ;
BEGIN
  {
 find the first record by retreiving with a search of GE and setting
    a key 
value < the first record key entry of the file }
  RetBuf.KeyNum[1] := 0 ;	{ lo
ad IDX key   for retreival of records }



PRM Program Example - Access to exis
ting files                          PAGE A-8



  RetBuf.Search := GE ;		{ s
et search type }
  RetBuf.KeySize := 1 ;		{ size of key data to search for }
 
 RetBuf.KeyData.Idx0 := '    ' ;  { set the key to blanks }
  RetBuf.RecSize :=
 ExaRecSize ; { may be destoyed, load each time }
  PrmRet ( FIND, IdxFile, Ret
Buf, RecBuf, Status ) ;	{ find 1st rec. }
 
  IF Status[1] < 1 
    THEN writ
eln('idx retreive error=',status[1], status[2])
    ELSE
      BEGIN
        
writeln ; writeln('begin xfer');
        i := 1 ;
        RetBuf.Search := NEX
 ;		{ set sequential mode of retrieval }
        REPEAT 
          RetBuf.RecS
ize := ExaRecSize ; { may be destoyed, load each time }
          PrmRet( GET, 
IdxFile, RetBuf, RecBuf, Status ) ; { get a record }
          IF Status[1] < 1
 
            THEN writeln('GET fail = ',status[1],status[2] )
            ELS
E
              BEGIN
                { no need to xfer buffer, seq and idx ha
ve same rec. buffers }
                RetBuf.RecSize := ExaRecSize ; { load ea
ch time }
                PRMSto ( PUT, SeqFile, SeqStoBuf, RecBuf, Status ) ;


                IF Status[1] < 1 
                  THEN writeln('PUT fail = '
,status[1],status[2] )
                  ELSE 
                    IF i < 5 TH
EN	{ Store 4 RFA's for retreival }
                    BEGIN
                 
     SeqRfas[i,1] := SeqStoBuf.RfaOut[1] ;  { save the RFA }
                  
    SeqRfas[i,2] := SeqStoBuf.RfaOut[2] ;  { save the RFA }
                   
   SeqRfas[i,3] := SeqStoBuf.RfaOut[3] ;  { save the RFA }
                    
  writeln('Stored at RFA=', SeqRfas[i,1]:4, 
                               Seq
Rfas[i,2]:4,SeqRfas[i,3]:4, ' data=',
                               RecBuf.Sec
Num, 
                               RecBuf.SecSup, recBuf.SecDesc ) ;
       
               i := i + 1 ;
                    END ;
              END ;
   
     UNTIL Status[1] = ErEof ;    { get all record, go till end-of-file }
     
   writeln('xfer from idx to seq complete') ;
      END ;	{ ELSE }
           

END;	{ PROCEDURE XferToSeq }
 
PROCEDURE RetByRfa ;
  PROCEDURE GetRecord (
 i : integer ) ;
  BEGIN
    RetBuf.KeyNum[1] := SeqRfas[i,1] ;  	{ load keynu
m with the rfa }
    RetBuf.KeyNum[2] := SeqRfas[i,2] ;  
    RetBuf.KeyNum[3]
 := SeqRfas[i,3] ;  
    RetBuf.RecSize := ExaRecSize ;	{ load each time }
   
 PrmRet( GET, SeqFile, RetBuf, RecBuf, Status ) ;	{ get the record }
    IF Sta
tus[1] >= 1 



PRM Program Example - Access to existing files                 
         PAGE A-9



      THEN		{ write the record }
        writeln('RFA 
NO.= ', SeqRfas[i,1]:4,
                SeqRfas[i,2]:4, SeqRfas[i,3]:3,' data='
,
                RecBuf.SecNum, RecBuf.SecSup, recBuf.SecDesc ) 
      ELSE
        writeln('RFA access error=',status[1],status[2]) ;
  END ;
BEGIN
  wr
iteln; writeln('Begin random retreival from a seq. file by RFA') ;
  RetBuf.Rec
Size := ExaRecSize ;	{ record size chg. by PRMRet that
                        
                  failed due to ErEof, must reload }
    RetBuf.Search := RFA ;
		{ set search to access by RFA }
    GetRecord ( 4 ) ;			{ get record spec. in
 array [4] }
    GetRecord ( 1 ) ;
    GetRecord ( 3 ) ;
    GetRecord ( 2 ) 
;
END;	{ PROCEDURE RetByRfa }
 
 
PROCEDURE RetRelative ;
BEGIN
  RetBuf.K
eyData.RecNum[1] := 1 ;	{ specify record number, 2 word }
  RetBuf.KeyData.RecN
um[2] := 0 ;
  RetBuf.Search := REC ;	{ search by a rec   vs. a string or RFA }

  RetBuf.RecSize := ExaRecSize ;
  PrmRet( FIND, RelFile, RetBuf, RecBuf, Sta
tus ) ;
  IF Status[1] < 1 
    THEN writeln (' fail to find 1st relative reco
rd, sts=',status[1] ) ;
 
  RetBuf.Search := NEX ;		{ switch from random to se
q search }
  writeln; writeln('Begin Relative File data retreival') ;
  IF Sta
tus[1] >= 1 
    THEN
      REPEAT	{ dump the entire file contents }
        
PrmRet( GET, RelFile, RetBuf, RecBuf, Status ) ;
        IF Status[1] >= 1 
  
        THEN writeln('data = ', RecBuf.SecNum, RecBuf.SecDesc ) 
          ELSE
 writeln('Get error=',status[1], status[2]);
      UNTIL Status[1] = ErEof ;  


END ;
 
BEGIN
  RMSIni ;			{ must specify before any rms ops }
  Openfiles 
;			{ open all the files }
  AddNewRec ( IdxFile, RecBuf, IdxStoBuf ) ;	{ add t
o indexed file }
  AddNewRec ( RelFile, RecBuf, IdxStoBuf ) ;	{ add to relative
 file }
  AddNewRec ( SeqFile, RecBuf, SeqStoBuf ) ;	{ add to sequential file }

  XferToSeq ;			{ transfer records from idex to seq. file }
  RetByRfa ;			{ 
retrieve random from seq. by RFA }
  RetRelative ;			{ retrieve all records fro
m relative file }
  PrmClo ( IdxFile ,status) ;	{ close all the files that are 
open }
  PrmClo ( RelFile ,status) ;
  PrmClo ( SeqFile ,status) ;



PRM Pro
gram Example - Access to existing files                         PAGE A-10





END.
 














                         APPENDIX B

      
  PRM Example of Creating an RMS Indexed File



 
PROGRAM Cre;
 
CONST
  NameSize	= 30 ;		{ sz of input file name, do not alter }
 
  { example label
s and sizes follow - user defines buffer sizes and labels }
  KeyXSize	= 2 ;		{
 user defines size of largest key }
  KeyYSize	= 6 ;		{ user defines these labe
ls and sizes }  
 
TYPE
 
  RecDef1 = RECORD	{ user defines field names and 
sizes }
    CASE integer OF	
      1 : (Dat1 : ARRAY [1..10] OF CHAR ;
      
     Dat2 : integer ) ;
      2 : (FYItem1 : ARRAY [1..30] OF CHAR ;
         
  FYItem2 : REAL ) ;
    END ;	{ User Defined Record }
 
 
 
 {************
***********************************************************
                   
  END PRM CONST and TYPE
 *****************************************************
****************** }
 
VAR
  FBuf		: RmsFileDesc ;		{ create buffer }
  RBuf
		: RecDef1 ;		{ record buffer }
  SBuf		: Storecord ;		{ storage desc. buffer 
}
  KBuf		: IdxKeyDesc ;		{ describe indexed file key }
  PrmStatus 	: RmsStat
us ;
 
 
{*******************************************************************
****
 *                 START PRM PROCEDURE CALLS                           *
 *********************************************************************** }
  
  
{ close the file }



PRM Example of Creating an RMS Indexed File          
                   PAGE B-2



PROCEDURE PRMClo ( VAR Filebuf : RmsFileDesc 
;	{ ref. to file to close }
                   VAR Status  : RmsStatus ) ;	{ ST
S and STV }
                   EXTERNAL ;
 
PROCEDURE PrmCre ( VAR CreBuf : R
msFileDesc ;
                   VAR Status : RmsStatus ) ;
                   
EXTERNAL ;
 
{ Define a single key of and indexed file, use in conj. with PrmC
re }
{ Define keys in ascending order starting with key 0 definition }
PROCEDU
RE PRMKey (VAR Filebuf : RmsFileDesc ;
                  VAR KeyBuf : IdxKeyDes
c ;
                  VAR Status  : RmsStatus ) ;	{ status of Sts and Stv }
  
                 EXTERNAL ;
 
{ Store a record in the specified file }
PROCED
URE PRMSto ( Operation   : RecOps ;	{ define PUT or UPDATE }
                  
 VAR FileBuf : RmsFileDesc ;	{ ref. to file for store }
                   VAR 
StoData : StoRecord ;	{ store variables }
                   VAR RecBuf  : RecD
ef1  ;	{ rec. buf connected to use }
                   VAR Status  : RmsStatus
);	{ STS and STV }
                   EXTERNAL ;
 
{ Define a routine to GET 
and DISPOSE heap space, execute first in root seg }
PROCEDURE RMSIni ; EXTERNAL
 ;
 
{***********************************************************************


 *                   END PRM PROCEDURE CALLS                           *
 ****
******************************************************************* }
  
  
 

BEGIN
  RMSIni ;			{ must be the first thing }
 
  { define the primary key
 }
  WITH KBuf DO
    BEGIN
      KeyNum := 0 ;
      KeyPos := 0 ;
      K
eySiz := 5 ;
    END ;
  PrmKey ( FBuf, KBuf, PrmStatus ) ;
 
  { define alt
ernate key  1 }
  WITH KBuf DO
    BEGIN
      KeyNum := 1 ;
      KeyPos :=
 3 ;
      KeySiz := 5 ;
    END ;
  PrmKey ( FBuf, KBuf, PrmStatus ) ;
 



PRM Example of Creating an RMS Indexed File                             PAGE B
-3



  { define alternate key  2 }
  WITH KBuf DO
    BEGIN
      KeyNum
 := 2 ;
      KeyPos := 4 ;
      KeySiz := 3 ;
    END ;
  PrmKey ( FBuf, K
Buf, PrmStatus ) ;
 
  { define alternate key  3 }
  WITH KBuf DO
    BEGIN


      KeyNum := 3 ;
      KeyPos := 8 ;
      KeySiz := 2 ;
    END ;
  Prm
Key ( FBuf, KBuf, PrmStatus ) ;
 
  WITH FBuf DO
    BEGIN
      Org := IDX 
;
      FileName := 'Cretst.IDX                    ' ;
      LogChan := 4 ;	
      RecordSize := 30 ;
      Allocation[1] := 10 ;
      Allocation[2] := 0 
;
      BucketSize := 2 ;
      Contiguous := 'Y' ;
    END ;	{ WITH FBuf } 


  PrmCre ( FBuf, PrmStatus ) ;
  writeln ( 'File CreTst.Idx created, sts=',prm
status[1],
                           '  stv=',prmstatus[2] ) ;
 
  { store a
 record }
  RBuf.Dat1 := 'file data ' ;
  RBuf.Dat2 := 64 ;
  SBuf.RecSize :=
 30 ;
  PrmSto ( PUT, FBuf, SBuf, RBuf, PrmStatus ) ;
  writeln ( 'Store data,
 sts=',prmstatus[1], '   stv=',prmstatus[2] ) ;
 
  PrmClo ( FBuf, PrmStatus )
 ;
  writeln ( 'File closed, sts=',prmstatus[1], '   stv=',prmstatus[2] ) ;
 


END.
 














                         APPENDIX C

    PR
M Example of Command and Overlay Description Files




     Six logical uni
t numbers are provided  by  default  for
each task.  Logical channel numbers 3 
and 4 are available to
the PRM user.  The other four are used  by  the  system 
 and
Pascal.  PRMExa requires 3 logical channel therefore UNITS=7
is specifed 
in the command file.
 
File : PrmExaBld.Cmd
 
PRMEXA/CP/FP,PRMEXA/-SP=PRMEXA
/MP
LIBR=RMSRES:RO:6
EXTSCT=$$HEAP:4000
UNITS=7
 
 
 
 
File : PrmExa.Od
l
 
	.ROOT PRMEXA-RMS-PAS-RMSROT-RMSALL
;
;	pascal interface to PRM routines

RMS:	.FCTR lb:[300,47]RMSPAS/LB
;
;	pascal libray
PAS:	.FCTR lb:[300,41]PAS
LIB/LB
;
;	overlay structure for resident library
@lb:[300,45]RMSRLX.ODL
	.E
ND