9/81


















                                 PRM-11 USER'S GUIDE

                           OMSI PASCAL INTERFACE TO RMS-11










                                  Kenneth G. Tibesar
                      3M Engineering Systems and Technology Labs
                              St. Paul, Minnesota 55144



        Pascal Record Management User's Manual                       Page 2
        Table Of Contents


          1.0 Introduction To PRM
            1.1 PRM Design
            1.2 User Interface
            1.3 File Operations
            1.4 Record Operations
            1.5 RFA
            1.6 Memory Requirements
          2.0 Preparing for PRM
            2.1 Pre-defined Data Structures
            2.2 Control Buffers
              2.2.1 RmsFileDesc - File Description
              2.2.2 RetRecord - Record Retrieval
              2.2.3 StoRecord - Record Storage
              2.2.4 IdxKeyDesc - Indexed Key Description
            2.3 Record Buffers
              2.3.1 Non-Shared Buffers
              2.3.2 Shared Buffers
            2.4 Key Buffers
            2.5 PRM External Calls
            2.6 Rms-11 Initialization
            2.7 Task Build
            2.8 User Space Optimization
            2.9 PRM Pit-Falls 
              2.9.1 Record Size
              2.9.2 Rms Initialization
              2.9.3 File Sharing
          3.0 Detailed Description of PRM Buffers
            3.1 RmsFileDesc - File Description
            3.2 RetRecord - Record Retrieval
            3.3 StoRecord - Record Storage
            3.4 IdxKeyDesc - Indexed Key Description
            3.5 User Defined Record Buffers
          4.0 Detailed Description of PRM Routines
            4.1 General Use
            4.2 File Access and Creation
              4.2.1 PRMClo
              4.2.2 PRMCre
              4.2.3 PRMKey
              4.2.4 PRMOpe
            4.3 Record Retrieval and Storage
              4.3.1 PRMDel
              4.3.2 PRMFre
              4.3.3 PRMRet
              4.3.4 PRMSto
           
          Appendix A  PRM program example - Access an existing RMS files
          Appendix B  PRM program example - RMS indexed file creation
          Appendix C  Command and Overlay descriptor files example
          Appendix D  PRM Error Codes
           



        Pascal Record Management User's Manual                       Page 3
          Preface


          PREFACE

               Record Management Services (RMS-11)  is  a  software  package
          written  and  supported  by DEC.  The package is a data management
          tool that supports sequential, relative and indexed (ISAM) files.

               Pascal  Record  Management  (PRM-11)   is   a   non-supported
          interface developed by 3M Engineering and Systems Technology Labs.
          PRM was developed as an interim until  the  OMSI  Pascal  Compiler
          directly supports RMS-11.  

               PRM was developed and tested using V1.2G of OMSI  Pascal  and
          DEC  RSX-11M+  operating  system.   Known problems will occur when
          using  OMSI  Pascal  V1.2H  due  to  changes   in   initialization
          procedures.   Version  2  of  OMSI  Pascal can be used only if the
          Version 1 switch is used.

               Comments and questions concerning PRM should be  directed  in
          writing to:
           
                            Kenneth Tibesar
                            3M Center, Bldg. 518-1
                            St. Paul, Minnesota 55144
           
                            Please - No Phone Calls
           














                         CHAPTER 1

                         Introduction to PRM




               PRM-11 is a set of routines written in OMSI  Pascal  with
          in-line  MACRO-11  code to interface to RMS-11.  DEC supported
          high level languages interface to RMS-11 by  using  key  words
          supported  by  the language compiler.  The present versions of
          OMSI Pascal for the PDP-11 do not  support  RMS-11  interface.
          PRM  provides  the  interface via a set of external procedures
          that are similiar to the key words used by DEC languages.  PRM
          routines  are  called  by the user code when RMS-11 operations
          are required.  The PRM routines are linked to  the  user  code
          during the task build.



          1.1  PRM Design


               PRM routines  use  DEC  supported  MACRO-11  routines  to
          perform  RMS-11  operations.  RMS-11 requires attribute blocks
          describing the file  (FAB)  and  record  (RAB).   PRM  defines
          fields  within  the  attribute  blocks.  This allows Pascal to
          directly control the contents of the files RABs and FABs.  The
          contents of the RABs and FABs are indirectly controlled by the
          PRM user by loading pre-defined buffers and using one  of  the
          PRM external procedures.

               User buffers required by PRM routines  are  allocated  in
          the  user  space.  The user defines only the number of buffers
          required for the application.  The buffers are loaded  by  the
          PRM  user  to  indicate file or record access parameters.  The
          buffers are also used by  PRM  as  working  space.   By  using
          buffers  allocated  globally (from the heap), PRM can preserve
          variables between PRM calls.

               Normally, RMS-11 requires the user to reserve POOL space.
          The  POOL  space  is  used  by  RMS  internal  code as control
          structures known as BDB's  (Buffer  Descriptor  Blocks).   The
          POOL  space  has  to  be  allocated  based  on  the  number of
          simultaneously opened files.  This  design  would  waste  user
          space that cannot be reclaimed even though the file is closed.



        Pascal Record Management User's Manual                 Page 1-2
        Introduction to PRM


          To avoid this loss of valuable  user  space,  PRM  dynamically
          allocates  and de-allocates the space when required by RMS-11.
          RMS-11 allows the MACRO-11 programmer to specify  a  GSA  (Get
          Space)  routine.   The PRM GSA routine simply calls the Pascal
          Run-Time-System NEW and DISPOSE routines to manage HEAP space.
          RMS-11  uses  the  declared  GSA  routine  when it requires or
          releases space.  Space is not used until a file is opened  and
          returned to the Pascal heap when the file is closed.

               PRM  was  modeled  after  syntax  used  by  existing  DEC
          supported  languages  that interface to RMS-11.  The following
          is a list of PRM and high level language comparisons:

               1.  DEC - Compilers support commands that perform  RMS-11
                   file and record operations.  

                        PRM - External procedures linked to  the  Pascal
                   program perform RMS-11 file and record operations.

               2.  DEC- Descriptive  key  words  are  used  with  RMS-11
                   commands to specify attributes of the file and record
                   operations.

                        PRM - Descriptive field names are used  to  load
                   records  passed  to  the  external  procedures.   The
                   record fields  specify  attributes  of  the  file  or
                   record operation.

               3.  DEC - A completion code  indicating  the  success  or
                   failure  of  each  RMS operation is made available to
                   the user.  The completion code is  available  through
                   the use of a reserved word.

                        PRM - A completion code is  returned  with  each
                   PRM call.  The code is the standard RMS-11 completion
                   code.  In addition, PRM provides debugging completion
                   codes for the PRM programmer.




          1.2  User Interface


               The PRM interface to OMSI Pascal uses the Pascal internal
          record  structure  to  pass  data.   Pre-defined  records  are
          included in the TYPE declaration of the User  Pascal  program.
          The Pascal programmer determines the operation to be performed
          (open, close, get record,  etc.)  and  loads  the  appropriate
          record  buffer.   Once loaded, the record address is passed to
          the specific PRM routine that  performs  the  file  or  record
          operation.   The  PRM  routines  load the RMS attribute blocks
          (RAB and/or FAB) with the control codes necessary  to  satisfy



        Pascal Record Management User's Manual                 Page 1-3
        Introduction to PRM


          the  user  request.  If data is to be stored or retrieved, the
          User Pascal program is also required to pass the address of  a
          data buffer.  The data buffer is loaded with data retrieved or
          the contents stored.

               In addition to control  and  data  buffer  addresses,  an
          address  of  a  status  buffer is required with all PRM calls.
          The status buffer is loaded with a completion code.  The  code
          is a standard MACRO-11 RMS success/error code (refer to RMS-11
          User's Manual, Appendix  B).   In  addition  PRM  will  return
          debugging  error  codes for the PRM user.  PRM error codes are
          only generated due to  PRM  user  program  procedural  errors.
          Refer to Appendix D for detail on PRM error codes.

               The user should check the completion code following  each
          PRM  call.   If  the  file  is  not opened properly, no record
          operations should be performed.  If the user  continues  after
          an error in a file open or creation, PRM will catch the error.
          All record operations on an improperly opened or created  file
          are   prohibited.    Any  call  that  attempts  access  to  an
          improperly opened file will be rejected and a PRM  error  code
          will be returned.



          1.3  File Operations


               There are four file  operation  primitives  provided.   A
          buffer  of  TYPE  RmsFileDesc  is  used  with all the PRM file
          routines.  The PRM user must allocate a buffer  of  this  TYPE
          for each simultaneously open file.  

               The buffer is loaded by the PRM user to describe the file
          to  be opened or created.  Once the file is open, the contents
          of this buffer provide space for the  file  attributes  blocks
          (FAB  and  RAB).   The  attributes  blocks  are  loaded by PRM
          routines to indicate PRM User  requests  to  RMS-11  routines.
          All  PRM  record  operations  require the PRM User to pass the
          address of the RmsFileDesc buffer.  This indicates to PRM  the
          file  to be accessed.  Space in the RMSFileDesc TYPE buffer is
          used is as the file and  record  attributes  blocks  (RAB  and
          FAB).  Allocation of user space for the file attributes blocks
          allows PRM to preserve the file and record attributes  between
          PRM calls.

               The file operation primitives are:

               1.  PRMClo - Closes an open RMS  file  and  returns  used
                   buffer space to the Pascal heap.

               2.  PrmCre - Creates an Rms File.   If  the  file  to  be
                   created is an indexed (ISAM) file, the PRMKey routine



        Pascal Record Management User's Manual                 Page 1-4
        Introduction to PRM


                   must be called a minimum of one time  prior  to  this
                   call.

               3.  PRMKey - Defines the keys of an indexed  file.   This
                   call  is used prior to the PRMCre routine.  Each call
                   defines a key of the  indexed  file.   Multiple  keys
                   must  be  defined in ascending order.  In addition to
                   the RMSFileDesc buffer, a buffer of  TYPE  IdxKeyDesc
                   is also used with the PRMKey routine.

               4.  PRMOpe - Opens an existing RMS file


               PRM insures that the user knows the file record  size  of
          the  file  specified for during PRMOpe.  The open requires the
          user to specify the record size of the file.   If  the  actual
          file  record  size  and  the user specified record size to not
          match, any activity on the file is prohibited.

               PRM returns the standard RMS-11 Macro error codes for all
          of the above calls.




               1.4  Record Operations


               There are four record operation  primitives  provided  by
          the  PRM  interface.   An  address of buffer TYPE RetRecord is
          passed to PRMRet.  An address  of  buffer  TYPE  StoRecord  is
          passed to PRMSto for storing records.  The buffers contain the
          necessary parameters for access to the file.  

               Record Operation PRM procedures require the user to  pass
          the  address  of  the  RMSFileDesc TYPE buffer with each call.
          The file RAB and FAB are defined for  the  open  file  in  the
          RMSFileDesc  buffer.  PRM interprets the user record operation
          request and loads the  appropriate  RAB  fields.   The  RMS-11
          Macro is then called and RMS-11 performs the record operation.

               Before the record  operations  are  performed,  PRM  will
          check  to  see  if the file to be accessed is properly opened.
          Record operations performed on an improperly opened file  will
          produce  unpredictable  results.  Any record operation request
          performed on an RMS file that has not been successfully opened
          by PRMOpe or PRMCre will be rejected by PRMRet and PRMSto.

               The record operation primitives are:

               1.  PRMDel - Delete the currently  selected  record  from
                   the   file.    The   currently   selected  record  is
                   established with a PRMRet call.



        Pascal Record Management User's Manual                 Page 1-5
        Introduction to PRM


               2.  PRMFre - Unlocks the bucket locked  by  the  previous
                   PRMRet  operation.   The bucket is locked only if the
                   file is opened with write access.

               3.  PRMRet - Retrieves a record from a file  successfully
                   opened with PRMOpe.  A record is always placed in the
                   RMS I/O internal buffer.  If a PGET type retrieval is
                   executed,  the  User Record Buffer (address passed by
                   the PRM user) is loaded.  If a PFIND  type  retrieval
                   is executed, the user record buffer is not loaded.

               4.  PRMSto - Store or update a record  in  a  sucessfully
                   opened  file.   A  PPUT operation will generate a new
                   record, a PUPDATE will update an existing record.




          1.5  RFA (Record File's Address)


               The PRM interface provides access  to  file  records  via
          RFA's.   An  RFA is a unique number assigned to each record of
          RMS type files.  The use of RFA provides direct  access  to  a
          record  by-passing  the record processing software.  Use of an
          RFA will also provide random access to  RMS  Sequential  files
          that are stored on random access devices (disks).

               An example of RFA access usage would  be  an  application
          that  searches  the file for records with specific conditions.
          The entire file is searched and  records  with  the  specified
          conditions are internally stored for future reference.  

               When the entire file has been  searched,  the  processing
          begins  randomly accessing the file for the specified records.
          If during the initial search, the RFA is stored, the  RFA  can
          be  used  to  randomly access the records.  The storing of the
          RFA may be an alternative to storing  the  entire  record  (or
          key)  in memory for rapid access to the data after the initial
          search.  Storing  the  entire  record  (or  key)  may  not  be
          possible due to space limitations.

               The previous scenario describes  the  use  of  DataTrieve
          when forming a "collection".


                                       NOTE

               The RFA used to define a record is unique and can be
               stored   in   a  file  for  access  to  records  for
               subsequent executions of an  application.   However,
               the  RFA  is  only  valid  for the life of the file.
               Once the file has been reorganized  with  a  utility



        Pascal Record Management User's Manual                 Page 1-6
        Introduction to PRM


               such as CNV or IFL, the RFA for a given record is no
               longer valid.



               RFA's can be used to retrieve  records  only.   When  you
          store  a  new  record,  PRM  returns the RFA generated by RMS.
          When you retrieve a record with normal access, the record  RFA
          is returned by PRMRet.  When you retrieve a record by RFA, you
          specify search = RFA in RetRecord buffer and load the  RFA  in
          KeyNum  in  RetRecord buffer.  Refer to paragraphs 3.2 and 3.3
          for description of the buffers used to pass RFA's between  PRM
          and the user code.  Refer to Appendix A for an example program
          using RFA random access with a sequential file.  



          1.6  Memory Requirements


               Additional code is required by any interface  to  RMS-11.
          Code  must  set-up  the  FAB  and  RAB  fields to indicate the
          request to RMS-11.  PRM code requires approximately 1KW if all
          routines are used.  PRM is designed so only the required calls
          are included.

               Dynamic memory space is managed by  the  Pascal  run-time
          system.  PRM defines a GSA routine (refer to paragraph 1.1) to
          efficiently control allocation and deallocation of Pascal heap
          space.

               RMS-11 code  requires  approximately  24KW  is  all  file
          organizations  with  all  RMS-11  file  and  record operations
          supported.  At present, PRM requests the task builder to  link
          ALL RMS-11 code to a PRM task.  If the RMS-11 Resident Library
          is not used, the user space remaining is severly limited.   If
          not  using  RMS-11 Resident Library support, modify the RMSIni
          routine  and/or  use  DEC  supplied  ODL  (overlay  descriptor
          language)  files.   Refer  to  paragraphs  2.5  and/or 2.6 for
          detail.














                         CHAPTER 2

                          Preparing for PRM




               The PRM User  Program  must  include  the  PRM  interface
          structures  and  external  procedure  calls in the User Pascal
          source program.  All the structures and calls are provided  as
          part  of  the PRM package.  The data structures are located in
          file PrmPrefix.Pas.  The PRM Procedure calls  are  located  in
          file PrmCalls.Pas.

               The following is an abbreviated list of  the  steps  that
          must be followed to prepare your task for interface to PRM-11.
          Paragraphs that follow detail each step.

               1.  Pre-Define  Data  Structures   -   Pre-defined   data
                   structures must be included in your source code.  The
                   data structure are located in file PRMPrefix.Pas.

               2.  Control Buffers - Allocate  space  in  your  task  by
                   defining  buffers  of  TYPES  defined  from  the data
                   structures  file.   The  buffers  are  used  to  pass
                   control  data  to PRM external routines.  Define only
                   the  buffers  required  to  satisfy   PRM   interface
                   requirements.

               3.  Record Buffers - Define data structures  to  describe
                   the  logical  record of your application.  An example
                   record definition is included in the data  structures
                   file.    Allocate  the  required  record  buffers  to
                   satisfy task requirements.

               4.  Key Buffers - Modify the KeyDef record definition and
                   keysizes  in  CONST  to  describe  the  keys  of your
                   indexed and/or relative file(s).  Use variant records
                   to  define  key(s)  of  the  RMS  file(s).   If  your
                   application uses  RELATIVE  type  files,  define  one
                   entry  of  type  "TwoWord"  (defined in PRMPrefix) to
                   hold RELATIVE record numbers for retrieval and  store
                   operations.  

               5.  External  Calls  -  Include  the  contents  of   file
                   PRMCalls.Pas.  Delete PRM procedure call(s) that will



        Pascal Record Management User's Manual                 Page 2-2
        Preparing for PRM


                   not be used.  This will avoid the  addition  of  code
                   that will not be used.

               6.  RMS-11 Initialization - Modify  RMSIni  if  all  file
                   organizations  and/or record operations are not used.
                   This is important  if  you  are  NOT  using  the  RMS
                   Resident Library.

               7.  Task Build - Reference object library  PRMPAS  during
                   task build.  

               8.  User Space Optimization  -  Share  control  and  data
                   buffers if space is limited.

               9.  PRM Pit-Falls - Check to  make  sure  your  task  has
                   specified the proper parameters to PRM.




          2.1  Pre-defined Data Structures


               File PRMPrefix.Pas defines all  of  the  data  structures
          that  are  used  to  pass user specified data to PRM routines.
          Data is transferred to external routines by passing an address
          reference  of  control  buffers  allocated in the main program
          space.  PRM routines expect a specific format  of  the  buffer
          therefore  PRM  external procedures and user programs must use
          formatted records.

               The buffer descriptions used  by  PRM  routines  and  PRM
          Users  are not exactly alike.  For example, PRM routines fully
          define the RAB and FAB in the RMSFileDesc buffers.   The  user
          RMSFileDesc  buffer  defines  the RAB and FAB as "work space".
          This difference allows the user to ignore  fields  within  the
          RAB  and  FAB.   The complexity of the user program is reduced
          because  pointer  types  in  the  RAB  and  FAB  are   defined
          externally  only.   Another  difference  is the record and key
          buffer definitions.  PRM determines the  size  by  using  size
          data  passed  by  the  user.  PRM has to depend on the user to
          specify the proper sizes.



          2.2  Control buffers


               The control buffers provide the  user  with  a  means  of
          specifying  control  data  to PRM external routines.  PRM uses
          the control data loaded by the user to  load  the  RMS-11  RAB
          (record  attributes  block)  and  FAB (file attributes block).
          Codes are generated by PRM to indicate  user  requests  passed



        Pascal Record Management User's Manual                 Page 2-3
        Preparing for PRM


          via the control buffer fields.



          2.2.1  RMSFileDesc - File Description


               The RMSFileDesc (RMS File  Description)  type  buffer  is
          allocated  by the user in the main program space (heap space).
          A buffer is allocated for each simultaneously open file (refer
          to  paragraph 2.2.9).  The buffer is loaded by the user before
          the PRMOpe (open file) procedure is called.  All proceding PRM
          calls  pass  the  address of this buffer to the PRM routine to
          indicate the file to be used for the  record  operation.   The
          RMSFileDesc buffer provides PRM with space that is used as the
          file RAB and FAB.  Since the buffer is allocated from the user
          space  (versus locally allocated), the contents of the RAB and
          FAB can be preserved between PRM calls.



          2.2.2  RetRecord - Retrieval Record


               The RetRecord (Retrieval Record) type buffer defines  the
          user retrieval parameters.  PRM also uses fields in the buffer
          to pass back control data to the  calling  program.   The  PRM
          user  loads the buffer prior to each PRMRet (record retrieval)
          call.



          2.2.3  StoRecord - Storage Record


               The StoRecord (Store  Record)  type  buffer  defines  the
          parameters  used  when  storing a record in an open file.  The
          buffer is used with PRMSto (store record) external  procedure.



          2.2.4  IdxKeyDesc - Indexed Key Description 


               The IdxKeyDesc (Indexed File Key Description) type buffer
          is  used  to  define  each key of a dynamically created RMS-11
          indexed file.  A buffer of this type is loaded prior to  using
          the PRMKey (key definition) external procedure.  



        Pascal Record Management User's Manual                 Page 2-4
        Preparing for PRM


          2.3  Record buffers


               The PRM user defines record  buffers  to  hold  the  file
          logical  records.  One record buffer can be allocated for each
          file or record buffers can be  shared.   The  address  of  the
          record  buffer  and size of the record buffer is passed to the
          PRMRet or PRMSto external procedures.  The external procedures
          use  the  size  and address of the buffer to load or store the
          data.  Size of the record buffer specified by the user  cannot
          be  checked  for accuracy by PRM external procedures.  If care
          the user specifies an incorrect buffer size, FATAL results can
          occur.  Refer to paragraph 2.2.9 for details.



          2.3.1  Non-shared record buffers


               If your program logic requires record data from more than
          one  file  simultaneously, serparate record buffers have to be
          allocated.  Buffers of the same type have to be  allocated  to
          satisfy  Pascal  type checking.  The type checking if enforced
          when passing the buffer to the external PRM procedures.

               Modify the RecDef buffer definition in  PRMPrefix.Pas  to
          satisfy  your  requirements.   Use  as  many  CASE  entries as
          required  to  specify  all  record  buffer  types.   If   your
          application  does  not  require the file full record, allocate
          the size of the buffer  required.   When  you  perform  record
          operation  specifying  a RecSize in the RetRecord or StoRecord
          buffers before the operation.

               In some cases, your application the record  buffer  sizes
          may  differ  significantly.  Using a variant record definition
          may not be desirable due to allocation of the largest  variant
          for  each  buffer.   This means that the smaller record buffer
          will have an unused space the size of the difference in record
          sizes.

               If the logical records of your application vary  in  size
          and  you  cannot afford wasted space, define a separate record
          TYPE for each record.  To satisfy Pascal  TYPE  checking  when
          the  buffer  is  passed to external PRM procedures, define the
          PRMRet and/or PRMSto call(s) local to a user  procedure.   The
          locally  defined  procedure  call  will  be  the  same  as the
          globally defined call with the exception of  the  record  TYPE
          definition.  The external procedure call will be linked to the
          same PRM external procedure by the task builder.



        Pascal Record Management User's Manual                 Page 2-5
        Preparing for PRM


          2.3.2  Shared record buffers


               If your application does not require data from  different
          files  simultaneously,  the  same record buffer can be used to
          hold data from more than one file.  A record buffer address is
          passed  to  PRM  procedures  that  store  (PRMSto) or retrieve
          (PRMRet) records.   The  record  buffer  used  is  dynamically
          determined by the calling program.



          2.4  Key Buffers


               Modify the KeyDef TYPE description to define the keys  of
          you  file(s).   A  CASE  of all the TYPEs can be defined.  The
          RetRecord type buffer uses the KeyDef description to determine
          the key structure.  Since the RetRecord places the KeyDef type
          field at the end of the RetRecord buffer, the key can  be  any
          size.  



          2.5  PRM External Calls


               External   procedure   calls   are   defined   in    file
          PrmCalls.Pas.   Only the calls used in your application should
          be included in  your  source  code.   The  task  builder  will
          include  the  PRM code form the PRM library for only the calls
          referenced in the source.  Define the PRM procedures local  to
          user procedures if different record TYPE buffers are required.
          Refer to paragraph 2.3.1 for details.



          2.6  RMS-11 Initialization


               There is only one initialization routine,  RMSIni.   This
          module  must  be  referenced  in  all tasks using PRM.  RMSIni
          defines a RMS-11 Macro that indicates to the task builder  the
          RMS-11  code  that  has  to  be  linked  to the task.  The PRM
          package  assumes  worst  case  and  specifies  that  all  file
          organizations with support for all operations.

               If the user links to the  RMS-11  Resident  library,  the
          support  of  one  or  all  file  organizations  and operations
          requires the same amount of space (8KW, 2 APR's) from the user
          task.  If the RMS-11 Resident library is not supported on your
          system, the RMS-11 code would require  approximately  24KW  of
          user space.



        Pascal Record Management User's Manual                 Page 2-6
        Preparing for PRM


               If you DO NOT link to the RMS-11  Resident  library,  you
          should do the following:

               1.  Make your own copy of file RMSIni.Src to be  used  by
                   your  task(s) with the same file access requirements.
                   Change  the  file  name  to  make  sure   your   task
                   references your copy of RMSIni.

               2.  Modify the entries following the $ORG  MACRO.   Refer
                   to  the  RMS-11  Macro-11 Reference Manual, paragraph
                   1.1.2.  Specify only  the  file  organization(s)  and
                   file access operations required by your task.

               3.  Compile and assemble the modified module.  

               4.  Reference the module in your source code.

               5.  Reference the modified module during the task build.

               6.  Use one of the standard RMS overlay descriptor files.
                   Refer to the RMS-11 User's Guide, chapter 8.


               In addition to indicating the code that is to  be  linked
          to the task, RMSIni also specifies a dynamic memory management
          routine.  The routine is defined  to  RMS-11  as  a  GSA  (Get
          Space) routine.

               It is essential that  RMSIni  be  located  in  the  .ROOT
          segment of an overlayed task.  The routine has to be available
          for RMS-11 at all times.  It is also essential that the RMSIni
          routine  be executed one time prior to any other PRM routines.



          2.7  Task Building 


               When task building, the PRMPAS.OLB must be referenced  in
          the  task builder command or overlay description file.  If you
          are using the RMS-11 Resident library, use  the  DEC  supplied
          overlay  description  and  reference  RMSRES  with  the RESLIB
          command file option.  If you are using overlays, select one of
          the standard DEC supplied overlay description files or use the
          DEC supplied command file MAKRMSODL.CMD to help tailor an  ODL
          file  to fit your specific needs.  An example of a command and
          ODL file is provided in Appendix C.



        Pascal Record Management User's Manual                 Page 2-7
        Preparing for PRM


          2.8  User Space Optimization


               If your application requires access to files that are not
          opened  simultaneously, file buffer of TYPE RmsfileDesc can be
          used for more than one file.  It is important that a  file  be
          closed  successfully  before  the  buffer  is used for another
          file.

               In most cases, the RetRecord and StoRecord  TYPE  buffers
          can  be  shared  with  no  problems.   Only  when  it  is more
          efficient to maintain access  attributes  for  separate  files
          should separate buffers be allocated.

               User record buffers can be shared  to  reduce  the  space
          used.   Paragraph 2.3 details shared and non-shard user record
          buffers.  

               The  RMSIni  routine  should  be  modified  to  fit  your
          application   requirements.    Paragraph   2.5  describes  the
          modifications to RMSIni.



          2.9  PRM Pit-Falls


               PRM routines perform error checking to make certain  that
          the  PRM User follows RMS-11 and PRM usage guide lines.  There
          are,  however,  certain  guidelines  that  cannot  be  checked
          because  PRM  routines  are  serperatly compilied.  PRM has to
          depend on the PRM user for items listed below.  If the minimum
          requirements  listed  below  are not met, unpredictable errors
          will result.



          2.9.1  Record Size


               PRM routines depend on the PRM User to supply the  record
          buffer.   The  user  also  has to supply PRM routines with the
          size of the record buffer.  Since PRM routines  are  external,
          compiled  separately  and a general set of routines supporting
          any RMS file, there is no way that the routines can accuratley
          check  buffer  sizes  allocated  in the MAIN PRM User program.
          PRM depends on the PRM User to inform the external routines of
          the  size of the record to be retrieved or stored.  If the PRM
          User defines a record size that  is  larger  than  the  record
          buffer  actually allocated, PRM (RMS) has to assume the record
          size is correct.  When a record is  retrieved  from  the  file
          user  code (or data) will be destroyed if the allocated buffer
          is smaller than the record retrieved from the file.



        Pascal Record Management User's Manual                 Page 2-8
        Preparing for PRM


               PRM  checks  the  user  record  size  specified  in   the
          RMSFileDesc  TYPE  buffer  when  the file is opened.  The user
          must specify the exact file record size.  This  is  to  ensure
          characteristics  of  the  file  being opened are known.  A PRM
          error code will be returned if  the  file  and  user  declared
          record  size do not match.  This, however, is only a check and
          does not ensure that user code will not be destroyed.  The PRM
          user  should  define  a  CONSTANT  to  define  the size of the
          logical record buffer.  The same  CONSTANT  should  be  loaded
          into the RMSFileDesc buffer before the PRMOpe.



          2.9.2  RMS Initialization


               If the RMSIni routine is not executed first in your task,
          unpredictable  results will occur.  RMS-11 assumes the the GSA
          routine (declared within  the  RMSIni  module)  is  constantly
          available  for  use.   If  the GSA routine is not in the .ROOT
          segment of your task, RMS-11 will fail.   Refer  to  paragraph
          2.4   for  detailed  information  concerning  modification  of
          RMSIni.



          2.9.3  File Sharing


               If the file being accessed is  to  be  used  by  multiple
          tasks simultaneously, and your tasks specifies write access to
          the file, the target bucket of a record access will be locked.
          When  a  bucket  is  locked, the records in the bucket are not
          accessable  by  other  users.   When  your   application   has
          completed  the  access (or timed-out if waiting for an event),
          the bucket should be released by executing the PRMFre routine.
          If your application specifies READ access to the file, buckets
          are never locked.














                         CHAPTER 3

                Detailed Description of PRM Buffers




               This chapter gives detailed description of  all  the  PRM
          pre-defined   buffers  that  have  to  be  used  for  the  PRM
          interface.  Brief descriptions of the fields  of  each  buffer
          are   provided.   Detailed  description  of  file  and  record
          attributes requested by each  field  can  be  located  in  the
          RMS-11 User's Guide.



          3.1  RmsFileDesc - File Description


               The following describes the  fields  in  the  RMSFileDesc
          type buffer that are used to create an RMS-11 file.  

               1.  ORG - File Organization

                   1.  Description  :   The  file  organization  of   an
                       existing  file  to  be  opened  or  a  file to be
                       created.  Use one of the key word scalar types to
                       define  a  Sequential  (SEQ),  Relative  (REL) or
                       Indexed (IDX) file.

                   2.  Default :  None


               2.  FileName - File Name 

                   1.  Description :  Full  file  specification  of  the
                       file  being  created.   The file specification is
                       defined by the operating system being used.

                   2.  Default :  None


               3.  LogChan - Logical Channel Number 

                   1.  Description :  The logical channel number for the
                       file  I/O  operations.  Refer to the task builder



        Pascal Record Management User's Manual                 Page 3-2
        Detailed Description of PRM Buffers


                       manual,  UNITS   description   in   the   Options
                       paragraph.

                   2.  Default :  None


               4.  Allow - System File Access

                   1.  Description :  What other tasks can  do  to  this
                       file  while  you have the file open.  If you want
                       exclusive access to the file specify NOSHARE.  If
                       you  will  allow others to open the file, specify
                       SHARE.  If any other task has  previously  opened
                       the  file with NOSHARE, an error will be returned
                       when you attempt to open the file.

                   2.  Default :  Share


               5.  Access - Program Access 

                   1.  Description :  Specifies what the program opening
                       the  file can do while the file is open.  Specify
                       PREAD for read only, PWRITE for  write  only  and
                       PBOTH  for both read and write access.  If either
                       PWRITE or PBOTH is specified, target buckets  are
                       locked.   The bucket remains locked until another
                       target bucket is specified or the PRMFre call  is
                       used.   If the file is shared, bucket locking for
                       long periods of time should be avoided.

                   2.  Default :  Read Only


               6.  RecordSize - File Record Size 

                   1.  Description :  The full size of the record of the
                       file  being  created  or  opened.  This should be
                       defined as a CONSTANT and also be used to  define
                       the  size  of the logical record buffer used.  If
                       an existing file is being opened, the exact  file
                       record  size  has  to be specified or a PRM error
                       code will be returned.

                   2.  Default :  None 


               7.  DeferWrite - Deferred Bucket Write to File

                   1.  Description :   Valid  for  indexed  files  only.
                       Normally  storage  of  each logical record causes
                       the contents of  the  entire  RMS  bucket  to  be
                       stored  in the file to ensure the contents of the



        Pascal Record Management User's Manual                 Page 3-3
        Detailed Description of PRM Buffers


                       file  contain  the  most  up-to-date  data.    If
                       deferred  write  is selected, the bucket will not
                       be written to the file until the bucket is full.

                   2.  Default :  No Deferred Write


               8.  Unlock - Unlock the file 

                   1.  Description :  The file will not be locked  as  a
                       result of the improper closing of the file due to
                       program abort.  This should NOT be used  for  RMS
                       Sequential files.

                   2.  Default :  Lock the file if improperly closed


               9.  ObeyFill - Obey Bucket Fill Number

                   1.  Description :  Each RMS bucket may  have  a  fill
                       number specified when the file is created.  Since
                       the PRM user cannot specify  the  value  of  this
                       parameter  during  PRMCre,  this  feature is only
                       valid when opening an existing file created  with
                       RMSDEF or RMSDFN.

                   2.  Default :  Fill the bucket as much as possible.


               10. MassInsert - Mass Insert records

                   1.  Description :  Used for RMS indexed  files  only.
                       Normally  RMS will traverse the indexed tree with
                       each record insert.  If this option is  selected,
                       the  record  is placed in the file at the present
                       pointer  location.   Extreme  caution  should  be
                       exercised  when  using this option.  Refer to the
                       RMS MACRO-11 Reference Manual for details.

                   2.  Default :  No mass insert


               11. FileEnd - File Pointer to End-Of-File

                   1.  Description  :   When  opening  an  existing  RMS
                       Sequential  file  this  option  can be used.  The
                       option will position the file pointer to the  end
                       of  the  file  in preparation for the addition of
                       records to the file.

                   2.  Default :  File pointer to the beginning  of  the
                       file.




        Pascal Record Management User's Manual                 Page 3-4
        Detailed Description of PRM Buffers


               12. RecForm - Logical Record Format

                   1.  Description :  The record format of fixed length,
                       variable   length   or   stream  format  records.
                       Specify FFIX for a fixed length record, FVAR  for
                       a  variable length record and FSTREAM (sequential
                       file only) for stream format.

                   2.  Default :  Fixed


               13. Allocation - File Block Initial Allocation

                   1.  Description :  The number  of  disk  blocks  that
                       should  be initially allocated to the file during
                       file creation.

                   2.  Default :  0 blocks


               14. BucketSize - RMS Bucket Size 

                   1.  Description :  A logical unit of storage for  RMS
                       files is known as the bucket.  Specify the number
                       of blocks for each bucket.

                   2.  Default :  1


               15. EXTQUA - Default Extension Quatity 

                   1.  Description  :   If  the  file   is   dynamically
                       extended,  this  number  specifies  the number of
                       blocks the file will be extended.  Should  always
                       be  specified  to  avoid  file header entries and
                       hence file access performance degradation.

                   2.  Default :  1 block extended


               16. Contiguous - Contiguous File

                   1.  Description :  The file  size  specified  by  the
                       allocation  field  is allocated in contigous disk
                       blocks.   If  the  contigous   blocks   are   not
                       available, an error is returned.  

                   2.  Default :  Non-contiguous


               17. Temporary - Temporary File

                   1.  Description  :   The   file   will   be   deleted



        Pascal Record Management User's Manual                 Page 3-5
        Detailed Description of PRM Buffers


                       automatically  by  the  operating system when the
                       file is closed.  The file is  in  existence  only
                       while the file is open.

                   2.  Default :  Permanent File





          3.2  RetRecord - Record Retrieval


               The following record fields contain data  that  interact.
          It  is  important  that  ALL  the required fields be loaded to
          satify  the  record  organization  and  record  access.    The
          following  gives  a  description  of  the  fields  in  the PRM
          retrieval buffer RetRecord:

               1.  KEYNUM - Key Number

                   1.  Indexed Key :  If the Search Type (defined below)
                       is  EQ,  GT  or GE then this entry is the Indexed
                       key number that RMS is to  use  for  data  record
                       retrieval.  This number can be 0 (primary key) to
                       n-1 where n is the number of keys in the  indexed
                       file.

                   2.  RFA :  If the Search Type (defined below) is  RFA
                       then  the Key Number is the RFA number.  Any file
                       organization  can  use  this  type   of   access.
                       Sequential  files  can use random access if using
                       RFA access.  Refer to paragraph 1.4 for details.

                   3.  Default :  None


               2.  SEARCH - Mode of Record Search

                   1.  EQ, GT, GE :  Search types of EQ, GT  or  GE  are
                       for access of Indexed records only.  These search
                       types  define   the   comparison   criteria   for
                       retrieving   records.   The  comparison  is  made
                       between the data in the  KEYDATA  field  of  this
                       buffer  (defined  below)  and the contents of the
                       file key data for the key specified in the KEYNUM
                       (defined above) field.

                   2.  RFA :  The RFA search type can be  for  any  file
                       organization.   The  KEYNUM  field must be loaded
                       with the RFA number.

                   3.  NEX :  The NEX search type can be used to  access



        Pascal Record Management User's Manual                 Page 3-6
        Detailed Description of PRM Buffers


                       the  NEXt  record in the file.  This mode is used
                       to sequential access records from a  Relative  or
                       Indexed file.  This is the only record access for
                       RMS Sequential files.  This mode  is  used  after
                       positioning  the record stream to a file position
                       using a random access search.  The random  access
                       search is executed using PrmRet witha GET or FIND
                       operation.

                   4.  REC :  The REC search  type  specifies  that  the
                       KEYDATA  field  (described  below)  is  a  record
                       number of a Relative file type.


               3.  RECSIZE - Logical Record Size 

                   1.  Input :  You must specify the size of the  record
                       you   want   retrieved   prior   to  each  PrmRet
                       operation.  Since the field is both an input  and
                       output,  the record size loaded will be destroyed
                       and therefore must be reloaded before each PRMRet
                       call.

                            RMS will transfer all or part of the  record
                       from  the  file.   If  you specify recsize < file
                       record size, only part  of  the  record  will  be
                       transferred  and  the  RMS  error  ERRTB  will be
                       returned.  If you specify recsize >  file  record
                       size,  the record buffer will be partially filled
                       with the record and PRM will  load  RECSIZE  with
                       the size of the record transferred to your record
                       buffer.

                            If you specify a  record  size  >  than  the
                       allocated buffer, PRM will assume the record size
                       to be correct.   The  record  will  destroy  data
                       following  the record buffer.  Refer to paragraph
                       2.9.1 for details.

                   2.  Output :  The size of the record  retrieved  from
                       the  RMS  file is loaded in this field and passed
                       back to the calling program.  This may be  useful
                       information  when  variable  length  records  are
                       used.


               4.  RFAOut - RFA output from PRM

                   1.  Description :  The  RFA  (Records  File  Address)
                       generated  by  RMS  is passed back to the calling
                       program.  For details on usage of RFA's refer  to
                       paragraph 1.4.  refer to paragraph 1.4.  




        Pascal Record Management User's Manual                 Page 3-7
        Detailed Description of PRM Buffers


               5.  KEYSIZE - Size of the key data

                   1.  Description :  Valid for indexed files only.   If
                       you  want  a  generic  search, specify the search
                       type of EQ, GT or GE then specify a key size that
                       is  <  the  full key size of the specified key in
                       KEYNUM.  For example, if the key data is for  zip
                       codes  and  you  want  all records with zip codes
                       that begin with 5501,  load  KEYDATA  with  5501,
                       search=EQ,  KEYSIZE=4,  execute  a PRMRet and the
                       first record in  the  file  with  5501x  will  be
                       returned.    Switch  to  sequential  access  (NEX
                       search type) and call PRMRet to  access  all  the
                       records within the generic zip code range.

                   2.  Default :  None


               6.  KEYDATA - String or Integer key data

                   1.  Indexed :  The string or integer value the PRMRet
                       operation  is  searching for in the indexed file.
                       RMS will search the file for a key  according  to
                       the  search  mode  specified  in the Search field
                       (above).

                   2.  Relative :  The relative record number of  a  RMS
                       relative file.





          3.3  StoRecord - Record Storage


               The  storage  type  operations  use  the  StoRecord  type
          buffer.  The following describes the StoRecord fields:

               1.  RecSize - Record Size

                   1.  Description :  The size of the  data  record  you
                       want  stored  in the RMS file.  You can specify a
                       record size <= to full record size for files with
                       variable record formats.  If you specify a record
                       size > the allocated record buffer, data that  is
                       not part of the logical record (garbage following
                       the record buffer) will be assumed as part of the
                       record.   The  record  stored in the file will be
                       corrupted.

                   2.  Default :  None




        Pascal Record Management User's Manual                 Page 3-8
        Detailed Description of PRM Buffers


               2.  RFAOut - The RFA generated by RMS-11 when the  record
                   was  stored  in  the  file.   The  RFA  can be stored
                   internally or in a file.  The RFA can then be used to
                   access the record if the file has not be reorganized.

               3.  KEY - RELATIVE Files only, The relative record number
                   of the target cell for the record to be stored.




          3.4  IdxKeyDesc - Indexed Key Description


               This buffer is used to define the keys of  a  dynamically
          created indexed file.  The buffer is loaded and PRMKey routine
          is called to describe each key of the file being created.  The
          keys must be defined in ascending order.

               The following describes the fields  of  the  record  type
          IdxKeyDesc:

               1.  KeyNum - Indexed Key Number

                   1.  Description :  The indexed key  number  that  the
                       record  describes.   This  can be any number from
                       0-255.  

                   2.  Default :  None


               2.  KeyPos - Key Position in the Record

                   1.  Description :  The starting byte position  (start
                       with 0) of the key in the logical record.

                   2.  Default :  None


               3.  KeySiz - Size of the Key

                   1.  Description :  Size in bytes of the key defined.

                   2.  Default :  None


               4.  KeyTyp - Key Type

                   1.  Description :  The key can be of type  string  or
                       integer.   Other  types of keys are available but
                       not supported by PRM.

                   2.  Default :  String



        Pascal Record Management User's Manual                 Page 3-9
        Detailed Description of PRM Buffers




               5.  KEYDUP - Duplicate Key

                   1.  Description :  If the key  being  defined  allows
                       duplicate entries, specify a "Y" in this field.

                   2.  Default :  No Duplicates


               6.  KEYCHG - Key value change 

                   1.  Description :  Valid for alternate keys only.  If
                       selected the value of the key may be altered on a
                       record update.  

                   2.  Default :  No Changes


               7.  KeyNul - Key Null value

                   1.  Description :  Valid for alternate keys only.  If
                       a  keyed field of the record is not valid for all
                       records in the file, a  null  key  value  can  be
                       specified.   If  a  null key value is defined and
                       the field if  FILLED  with  the  null  key  value
                       during  a record insert (PRMSto - PUT) there will
                       be no entry in the alternate key structure.  

                            Example:  A file has a key in  an  employees
                       record   describing   the  name  of  the  company
                       softball ball team the employee  belongs  to.   A
                       null  key  value  should  be  specified  so  that
                       unneccessary entries in the  tree  structure  for
                       the  alternate  key are not entered for employees
                       that do not belong to a team.

                   2.  Default :  No Null





          3.5  User Defined Record Buffers


               The RecDef Record TYPE has to be modified to  define  the
          fields  of  your logical record.  Multiple CASE entries can be
          used to define all the logical records.  Once  the  buffer  is
          defined, one or more record buffers should be allocated in the
          user space.  Refer to paragraph 2.3 for more detail.














                         CHAPTER 4

                Detailed Description of PRM Routines




               This chapter describes the PRM calls  used  to  interpret
          the User's request and pass the request to RMS-11.



          4.1  General Use


               To use any of the  PRM  calls,  the  user  must  properly
          prepare  the  task  with  the proper buffer types and external
          calls.  The following list the coding rules to follow for  PRM
          calls:

               1.  The RMSIni routine must be executed before any  other
                   PRM routine is called.

               2.  The calling routines must  be  OMSI  Pascal  V1.   If
                   Pascal  V2.0  is  used,  the version 1 switch must be
                   used on the external call.  Pascal V1.2H code has not
                   been  tested.   If  used, specify the contents of all
                   fields rather than taking the defaults.

               3.  Once a file has  been  opened,  file  work  space  is
                   allocated  in  the  buffer  of  TYPE  RmsFileDesc you
                   provide on the open.  This buffer  is  used  for  all
                   file operations on that file.

               4.  A variable of TYPE RMSStatus word should  be  checked
                   after  ALL  PRM calls.  The value of +1 will indicate
                   success, a negative value will indicate failure.  

                        The negative value can be a PRM error or an  RMS
                   type  error.   If  an RMS error, word 1 of the status
                   will be loaded with the RMS STS and word 2  with  the
                   RMS  STV  value.   Definition  of these errors can be
                   found in the RMS User or RMS Macro Reference Manuals.
                   The PRM returned error codes are defined in the CONST
                   section of PRMPrefix.Pas and Appendix D.



        Pascal Record Management User's Manual                 Page 4-2
        Detailed Description of PRM Routines


               5.  Do not perform any record operations unless the  file
                   has  been  properly  opened  and initialized.  If PRM
                   routines (PRMOpe or PRMCre) do not successfully  open
                   the  RMS  file  all  PRM  record  operations  will be
                   inhibited and error code PrIni will  be  returned  in
                   word   1   of  the  status.   If  PRM  allows  record
                   operations   on   an    inproperly    opened    file,
                   unpredictable results could occur.

               6.  If the RmsFileDesc buffer is used for multiple files,
                   care  must  be  used.   When  using  the  buffer  for
                   multiple files, be sure  to  close  the  file  before
                   re-use.   When  the  buffer  is available, reload the
                   buffer with the new parameters describing the file.




          4.2  File Access and Creation


               The following paragraphs describe the PRM  routines  that
          are  used  to open or create RMS-11 files.  All file types are
          supported for both the access to existing files  and  creation
          of  new  files.   The following describes the requirements for
          the use of each file  type  external  procedure  and  possible
          errors that can occur from their use.

               Detail on each of  the  File  Operations  for  each  file
          organization is located in the RMS-11 User's Guide.



          4.2.1  PrmClo 


               This procedure is used to close an open  RMS  file.   The
          RMSFileDesc  type buffer passed to the procedure specifies the
          file to be closed.  The RMS Sts  and  Stv  values  are  passed
          backed to the calling program.  These values should be checked
          to insure the close was successful.



          4.2.2  PrmCre


               This procedure is used to dynamically create an RMS file.
          All  file  organizations can be created by simply defining the
          file type you want created  and  loading  the  remaining  file
          creation fields in the RMSFileDesc record.  For creation of an
          indexed file, the PRMKey routine must be called at  least  one
          time (define primary key) before calling the PRMCre routine.



        Pascal Record Management User's Manual                 Page 4-3
        Detailed Description of PRM Routines


          4.2.3  PrmKey


               This call is used  when  you  desire  to  create  an  RMS
          indexed  file.   Call PrmKey to define each key of the indexed
          file prior to the PrmCre call.  PrmKey can be called  multiple
          times defining a new key with each call.  The keys are defined
          in a buffer of type IdxKeyDesc.  When defining more  than  one
          key,  define  the  keys  in  ascending order starting with the
          primary key (key 0).  RMS will generate an error on the create
          if you do not follow this convention.



          4.2.4  PrmOpe 


               This procedure will open an exising RMS type  file.   The
          file  can be previously defined with an RMS utility (RMSDef or
          RMSDfn) or by any other program that has  created  the  RMS-11
          file.

               When the file is opened,  PRM  FATAL  conditions  may  be
          detected.   The  error  is  the  result  of  not following PRM
          conventions.  The error code is returned in the PrmStatus.   A
          description  of  these error codes is described in Appendix D.
          These types of errors should be corrected immediately.

               If  PrmOpe  does  not  properly  initialize,  ALL  record
          operations  on  the  file  will  be  rejected  by  PRM  record
          operations.  This feature is for the  user  that  ignores  the
          error codes returned from PrmOpe.  If the file is not properly
          opened and record operations are performed, the task may abort
          with  ODD  ADDRESS (or other) type fatal errors.  A recordsize
          specified in the RmsFileDesc buffer <>  file  record  size  is
          considered improper initialization.



          4.3  Record Access and Storage


               The following describes all record  operations  supported
          by  PRM.  The record operations are described here in terms of
          the PRM interface.  Detailed information describing the record
          operation  for  each  file  organization can be located in the
          RMS-11 User's Manual.



        Pascal Record Management User's Manual                 Page 4-4
        Detailed Description of PRM Routines


          4.3.1  PrmDel 


               This procedure is used  to  delete  a  record  previously
          located with a SUCCESSFUL PrmRet PGET or PFIND operation.  The
          user should make  sure  that  the  file  pointer  is  properly
          positioned  before  calling this procedure.  That is, the user
          must  check  the  PrmStatus  code  returned  from  the  PrmRet
          operation for a success code (+1) before calling PrmDel.



          4.3.2  PrmFre 


               This procedure is used to unlock a bucket so other  tasks
          can  access records in the bucket.  Buckets are locked only if
          the file is opened with ACCESS of PWRITE or PBOTH.  The Access
          field  default  of  Read  only  should  be  selected  if  your
          application is only going to read data.  The PREAD file access
          will not lock buckets.

               If you specify a write  or  read/write  access,  the  RMS
          bucket will be locked when you access records in the bucket of
          the file.  The lock will remain on the bucket  until  1)  your
          application  accesses  another  record  not  in  the presently
          locked bucket, 2) your application closes the file or 3)  your
          application executes the PrmFre call.

               If your application is updating or writing records  in  a
          shared  file,  this  call should be kept in mind.  The call is
          especially useful when dealing with interactive type programs.
          The  operator  response  should be timed if the application is
          holding a bucket locked and the continuation of the program is
          dependant  on the operator (who may have just gone on a coffee
          break).



          4.3.3  PrmRet 


               This call is used to retrieve a record  from  a  properly
          opened  RMS file.  Before access to the RMS file is attempted,
          a check is made to see if  PrmOpe  has  been  called  and  has
          properly  opened  the  file.   If the file has not been opened
          properly, a FATAL message  will  be  printed  and  the  RMSRet
          operation will not be performed.

               Load the RetRecord buffer prior to using this call.  With
          the  call, specify a PGET or PFIND record operation.  Refer to
          the RMS-11 User's Guide for detail  concerning  GET  and  FIND
          record operations.



        Pascal Record Management User's Manual                 Page 4-5
        Detailed Description of PRM Routines


          4.3.4  PrmSto 


               This procedure is used to store a record in a  file  that
          has  been  properly  opened with PrmOpe or PrmCre.  The PrmSto
          Call defines the type of operation with the  first  parameter.
          If the PrmSto describes an PUPDATE, the store must be preceded
          by a successful  PRMRet  operation.   If  you  define  a  PPUT
          operation,  the  record in stored in a new location in the RMS
          file.  Refer to the RMS-11 User's Guide for detail  concerning
          the PUT and UPDATE record opeations.















                         APPENDIX A

         PRM Program Example - Access to existing files




            
      PROGRAM PrmExample ;
       
      {
       AUTHOR :	Ken Tibesar
      		ES and T Labs - Bldg. 518-1
                      3M Company St. Paul
       
       SYSTEM REQUIREMENTS:
      		RSX-11M+ OPERATING SYSTEM
       		OMSI V1.2G PASCAL COMPILER
      		RMS-11 RECORD MANAGEMENT WITH
      		   PRM (Pascal Record Management created by 3M)
       
       BUILD PROCEDURE :  Refer to Appendix C
       
       PROGRAM DESCRIPTION:
           This program shows access to the three types of RMS files.  
       The files are created before the program executes.  The program
       shows the following:
        1. Open of an existing file.
        2. Adding records to each file type.
        3. Transferring records from seq. file to idx file.
        4. Access to seq. file by RFA.
        5. Access to rel. file.
        6. Close the files.
      }
        
      CONST
        IdxLch = 3 ;		{ of the first 6 UNITS } 
        RelLch = 4 ;		{ ch. 3  4 avail. by default }
                              _
        SeqLch = 7 ;		{ must spec. UNITS=n for units > 6 }
       
        
        NameSize	= 30 ;		{ size of the file name }
        ExaRecSize	= 28 ;		{ full record size }
       
      TYPE
        RecDef	= RECORD	{ user defined record type  1 }



      PRM Program Example - Access to existing files               Page A-2



          SecNum	: ARRAY [1..4] OF CHAR ;{ section number }
          SecSup	: ARRAY [1..3] OF CHAR ;{ sup initials }
          Fill	: char ;
          SecDesc	: ARRAY [1..20] OF CHAR 
        END ; { RECORD }
       
        TwoWord = ARRAY [1..2] OF integer ;	{ record number size }
        KeyDef	= RECORD
          CASE integer OF 
            1 : ( Idx0 : ARRAY [1..Key0Size] OF CHAR) ; 
            2 : ( Idx1 : ARRAY [1..Key1Size] OF CHAR) ; 
            3 : ( RecNum : TwoWord ) ;  { REL file rec.   }
          END ;
       
      {****************************************************************
                           BEGIN PRM CONST and TYPE
                            file: PrmPrefix.Pas
       ****************************************************************
      }
        
      CONST
        { * Error values returned in status word 1 and word 2.
          * All errors set Status[1] to a negative value.
          * Refer to Appendix B of RMS User's Guide or App. D of this
            document.
        }
        PrINI	= -5001 ;
        PrRNE	= -5002 ;
        PrRsz	= -5003 ;
        PrKY0	= -5004 ;
        PrKNS	= -5005 ;
        PrAsc	= -5006 ;
        ErDup	= -544 ;
        ErEof = -592 ;
        ErFac = -656 ;
        ErFnf = -736 ;
        ErRlk = -1440 ;
        ErRnf = -1472 ;
       
       
      TYPE
        RmsFileName	= ARRAY [1..NameSize] OF CHAR ;
        RmsStatus	= ARRAY [1..2] OF integer ;
       
        OrgTypes	= (SEQ,REL,IDX) ;
        AllowTypes	= (Share,NoShare) ;      
        AccessTypes	= (PRead,PWrite,PBoth) ; 
        FormType = (FFIX,FVAR,FSTREAM) ;{ record format type }
       
        RmsFileDesc	= RECORD
          Org		: OrgTypes ;	{ spec. file type }
          FileName	: RmsFileName ;	
          LogChan	: integer ;	{ spec. ch. n }



      PRM Program Example - Access to existing files               Page A-3



          Allow	: AllowTypes ;	{ what others may do }
          Access	: AccessTypes ;	{ what you may do }
          RecordSize  : INTEGER ;	{ full rec. size }
          Windows	: INTEGER ;	{ no. of ret. windows }
       
          { enable options with a capital "Y" }
          DeferWrite	: CHAR ;{ IDX, defer write }
          Unlock    	: CHAR ;{ REL  IDX, don't lock }
                                   _
          ObeyFill	: CHAR ;{ obey bucket fill no. }
          MassInsert	: CHAR ;{ ref. rms-11 ref. man. }
          FileEnd	: CHAR ;{ SEQ only, place at end }
       
          { file creation fields }
          RecForm	: FormType ;	{ rec. format }
          Allocation  : TwoWord ;	{ no. blocks allocated }
          BucketSize	: integer ;	{ data bucket size }
          ExtQua	: integer ;	{ no. blks extend file }
          { Enable following with capital "Y", if not loaded, }
          Contiguous	: CHAR ;	{ create contiguous file }
          Temporary	: char ;	{ delete file when closed }
       
          WorkSpace	: PACKED ARRAY [1..160] OF char ;
        END ;	{ RmsFileDesc Record }
       
        SearchTypes	= (EQ,GT,GE,RFA,NEX,REC) ; 
        ThreeWord	= ARRAY [1..3] OF Integer ;{ for RFA's }
        RecOps	= (PGET,PFIND,PPUT,PUPDATE) ; 
        RetRecord = RECORD
          { - USE with PRMRET, INPUT - to GET and FIND }
          KeyNum	: Threeword ;	{ INPUT- IDX Key   or RFA }
          Search	: SearchTypes ;	{ INPUT - spec. search opr }
          RecSize	: integer ;	{ INPUT - sz rec. to PGET
                                        OUTPUT- sz rec. returned }
          RFAout	: ThreeWord ;	{ OUTPUT- valid if <> RFA }
          KeySize	: integer ;	{ INPUT - size of key data }
          KeyData	: KeyDef ;	{ INPUT - key string or rec.   }
        END ;	{ RetRecord RECORD Definition }
       
        StoRecord = RECORD
            { USE with PRMSTO, Input to PUT and UPDATE }
            RecSize	: integer ;	{ INPUT - spec. rec. buffer }
            RFAOut	: ThreeWord ;	{ OUTPUT - record rfa }
            Cell	: KeyDef ;	{ INPUT - REL cell no. }
          END ;	{ StoRecord Record }
       
        {*****************************************************
       *                   END PRM CONST and TYPE             *
       *******************************************************}
        
       
       
      VAR
        chtfile	: text ;



      PRM Program Example - Access to existing files               Page A-4



        Rlen		: integer ;
        i		: integer ;
        SeqRfas	: ARRAY [1..4] OF ThreeWord;	
       
        IdxFile	: RmsFileDesc ;	{ file parameters }
        IdxStoBuf	: StoRecord ;	{ store buffer }
       
        RelFile	: RmsFileDesc ;	{ file parameters }
       
        SeqFile	: RmsFileDesc ;	{ file parameters }
        SeqStoBuf	: StoRecord ;	{ buf sequential file }
       
        RecBuf        : RecDef ; { same record buffer all files }
        RetBuf        : RetRecord ; { retreival buf for all file }
        RfaBuf	: Threeword ; { returned rfa }
        Status	: RmsStatus ; { rms status codes }
       
       
      { close the file }
      PROCEDURE PRMClo ( VAR Filebuf : RmsFileDesc ;	
                         VAR Status  : RmsStatus ) ;	{ STS and STV }
                         EXTERNAL ;
       
      { Delete a record }
      PROCEDURE PRMDel ( VAR FileBuf : RmsFileDesc ;
                         VAR Status  : RmsStatus ) ;	{ STS and STV }
                         EXTERNAL ;
       
      { Open an RMS Indexed file previously defined with RMSDEF }
      PROCEDURE PRMOpe ( VAR FileBuf : RmsFileDesc ;   
                         VAR Status  : RmsStatus ) ;	{ Sts and Stv }
                         EXTERNAL ;
       
      { Record retrieval from the specified file }
      PROCEDURE PRMRet( Operation : RecOps ;		
                         VAR FileBuf : RmsFileDesc ;	
                         VAR RetData : RetRecord ;	
                         VAR RecBuf  : RecDef  ;	
                         VAR Status  : RmsStatus ) ;	
                         EXTERNAL ;
       
      { Store a record in the specified file }
      PROCEDURE PRMSto ( Operation   : RecOps ;	
                         VAR FileBuf : RmsFileDesc ;	
                         VAR StoData : StoRecord ;	
                         VAR RecBuf  : RecDef ;	
                         VAR Status  : RmsStatus);	
                         EXTERNAL ;
       
      PROCEDURE RmsIni ; EXTERNAL ;
       
       
      PROCEDURE OpenFiles ;



      PRM Program Example - Access to existing files               Page A-5



      BEGIN
       
      { open an rms indexed file }
      WITH IdxFile DO
        BEGIN
          Org := IDX ;			
          FileName :=   '[300,47]PrmExa.Idx            ' ; 
          LogChan := IdxLch ;			
          Access := PBoth ;			
          RecordSize := ExaRecSize ;		
        END ;
      { all fields not specified will take their default condition }
      PrmOpe ( IdxFile, Status ) ;
      IF Status[1] < 1 
        THEN writeln('Idx Open error, code=',Status[1], Status[2] ) ;
       
      { open and rms relative file }
      WITH RelFile DO
        BEGIN
          Org := REL ;
          FileName :=   '[300,47]PrmExa.Rel            ' ;
          LogChan := RelLch ;
          Access := PBoth ;			
          RecordSize := ExaRecSize ;
        END ;
      PrmOpe ( RelFile, Status ) ;
      IF Status[1] < 1 
        THEN writeln('Rel Open error, code=',Status[1], Status[2] ) ;
       
      { open an rms sequential file }
      WITH SeqFile DO
        BEGIN
          Org := SEQ ;
          FileName := '[300,47]PrmExa.Seq            ' ;
          LogChan := SeqLch ;
          Access := PBoth ;			
          SeqFile.FileEnd := 'Y' ;		
          RecordSize := ExaRecSize ;
        END ;
      PrmOpe ( SeqFile, Status ) ;
      IF Status[1] < 1 
        THEN writeln('Seq Open error, code=',Status[1], Status[2] ) ;
       
      END ;	{ PROCEDURE Openfiles }
       
       
      PROCEDURE AddNewRec ( VAR TarFile : RmsFileDesc ; 
                            VAR TarRec : RecDef ;
                            VAR TarStoBuf : StoRecord ) ;
        PROCEDURE StoreIt ;
        BEGIN
          TarStoBuf.RecSize := ExaRecSize ;	{ specify each time }    
          PRMSto ( PPUT, TarFile, TarStoBuf, RecBuf, Status ) ;



      PRM Program Example - Access to existing files               Page A-6



          writeln('store ', status[1],status[2]);
        END ;
       
      BEGIN
        TarStoBuf.RecSize := ExaRecSize ;	
       
        { load the record buffer }
        TarRec.SecNum := '86A ' ;
        TarRec.SecSup := 'AAC' ;
        TarRec.SecDesc := 'Optical Inspection  ' ;                   
        StoreIt ;
       
        TarRec.SecNum := '86C ' ;
        TarRec.SecSup := 'TMT' ; 
        TarRec.SecDesc := 'Ultrasonic Process  ' ;
        StoreIt ;
       
        TarRec.SecNum := '86B ' ;
        TarRec.SecSup := 'WHO' ;
        TarRec.SecDesc := 'Computer Nurds      ' ;                   
        StoreIt ;
       
      END ;	{ PROCEDURE AddNewRec }
       
      PROCEDURE XferToSeq ;
      BEGIN
        { find the first record by retreiving with a search of 
          GE and setting a key value < the first record key 
          entry of the file }
        RetBuf.KeyNum[1] := 0 ;	{ load IDX key   }
        RetBuf.Search := GE ;		{ set search type }
        RetBuf.KeySize := 1 ;		{ size of key data }
        RetBuf.KeyData.Idx0 := '    ' ;  { set the key=blanks }
        RetBuf.RecSize := ExaRecSize ; { load each time }
        PrmRet ( PFIND, IdxFile, RetBuf, RecBuf, Status ) ;	
       
        IF Status[1] < 1 
          THEN writeln('idx retreive error=',status[1], status[2])
          ELSE
            BEGIN
              writeln ; writeln('begin xfer');
              i := 1 ;
              RetBuf.Search := NEX ;	{ set sequential mode }
              REPEAT 
                RetBuf.RecSize := ExaRecSize ; { load each time }
                PrmRet( PGET, IdxFile, RetBuf, RecBuf, Status ) ; 
                IF Status[1] < 1 
                  THEN writeln('GET fail = ',status[1],status[2] )
                  ELSE
                    BEGIN
                      RetBuf.RecSize := ExaRecSize ; { load each time }
                      PRMSto ( PPUT, SeqFile, SeqStoBuf, RecBuf, Status ) ;
                      IF Status[1] < 1 



      PRM Program Example - Access to existing files               Page A-7



                        THEN writeln('PUT fail = ',status[1],status[2] )
                        ELSE 
                          IF i < 5 THEN	
                          BEGIN
                            SeqRfas[i,1] := SeqStoBuf.RfaOut[1] ;  
                            SeqRfas[i,2] := SeqStoBuf.RfaOut[2] ;  
                            SeqRfas[i,3] := SeqStoBuf.RfaOut[3] ;  
                            writeln('Stored at RFA=', SeqRfas[i,1]:4, 
                                  SeqRfas[i,2]:4,SeqRfas[i,3]:4, ' data=',
                                  RecBuf.SecNum, 
                                  RecBuf.SecSup, recBuf.SecDesc ) ;
                            i := i + 1 ;
                          END ;
                    END ;
              UNTIL Status[1] = ErEof ;    
              writeln('xfer from idx to seq complete') ;
            END ;	{ ELSE }
                 
      END;	{ PROCEDURE XferToSeq }
       
      PROCEDURE RetByRfa ;
        PROCEDURE GetRecord ( i : integer ) ;
        BEGIN
          RetBuf.KeyNum[1] := SeqRfas[i,1] ;  	
          RetBuf.KeyNum[2] := SeqRfas[i,2] ;  
          RetBuf.KeyNum[3] := SeqRfas[i,3] ;  
          RetBuf.RecSize := ExaRecSize ;	{ load each time }
          PrmRet( PGET, SeqFile, RetBuf, RecBuf, Status ) ;	
          IF Status[1] >= 1 
            THEN		{ write the record }
              writeln('RFA NO.= ', SeqRfas[i,1]:4,
                      SeqRfas[i,2]:4, SeqRfas[i,3]:3,' data=',
                      RecBuf.SecNum, RecBuf.SecSup, recBuf.SecDesc ) 
            ELSE
              writeln('RFA access error=',status[1],status[2]) ;
        END ;
      BEGIN
        writeln; writeln('Begin random 
                         retreival from a seq. file by RFA') ;
        RetBuf.RecSize := ExaRecSize ;	
          RetBuf.Search := RFA ;	{ set search to access by RFA }
          GetRecord ( 4 ) ;		{ get record spec. in array [4] }
          GetRecord ( 1 ) ;
          GetRecord ( 3 ) ;
          GetRecord ( 2 ) ;
      END;	{ PROCEDURE RetByRfa }
       
       
      PROCEDURE RetRelative ;
      BEGIN
        RetBuf.KeyData.RecNum[1] := 1 ;	{ specify record no. }
        RetBuf.KeyData.RecNum[2] := 0 ;
        RetBuf.Search := REC ;	{ search by a rec   }



      PRM Program Example - Access to existing files               Page A-8



        RetBuf.RecSize := ExaRecSize ;
        PrmRet( PFIND, RelFile, RetBuf, RecBuf, Status ) ;
        IF Status[1] < 1 
          THEN writeln (' fail to find 1st 
                          relative record, sts=',status[1] ) ;
       
        RetBuf.Search := NEX ; { switch from random to seq search }
        writeln; writeln('Begin Relative File data retreival') ;
        IF Status[1] >= 1 
          THEN
            REPEAT	{ dump the entire file contents }
              PrmRet( PGET, RelFile, RetBuf, RecBuf, Status ) ;
              IF Status[1] >= 1 
                THEN writeln('data = ', RecBuf.SecNum, RecBuf.SecDesc ) 
                ELSE writeln('Get error=',status[1], status[2]);
            UNTIL Status[1] = ErEof ;  
      END ;
       
      BEGIN
        RmsIni ;		{ must specify before any rms ops }
        Openfiles ;			{ open all the files }
        AddNewRec ( IdxFile, RecBuf, IdxStoBuf ) ;	
        AddNewRec ( RelFile, RecBuf, IdxStoBuf ) ;	
        AddNewRec ( SeqFile, RecBuf, SeqStoBuf ) ;	
        XferToSeq 	{ transfer records from idex to seq. file }
        RetByRfa ;	{ retrieve random from seq. by RFA }
        RetRelative ;	{ retrieve all records from relative file }
        PrmClo ( IdxFile ,status) ;	{ close all the files }
        PrmClo ( RelFile ,status) ;
        PrmClo ( SeqFile ,status) ;
      END.
       














                         APPENDIX B

           PRM Example of Creating an RMS Indexed File




           PROGRAM CREIDX ;
       
      { 
       AUTHOR :	Ken Tibesar
      		ES and T Labs - Bldg. 518-1
                      3M Company St. Paul
       
       SYSTEM REQUIREMENTS:
      		RSX-11M+ OPERATING SYSTEM
       		OMSI V1.2G PASCAL COMPILER
      		RMS-11 RECORD MANAGEMENT WITH
      		   PRM (Pascal Record Management created by 3M)
       
       BUILD PROCEDURE :  Refer to Appendix C
       
       PROGRAM DESCRIPTION :
           This program is an example of dynamic definition and creation
       of an RMS Indexed File.  The program defines 4 keys of an indexed
       file, stores 1 record and closes the file. Status codes are 
       displayed after each PRM call. }
       
      CONST
        NameSize	= 30 ;	{ sz of input file name, do not alter }
       
      TYPE
       
        { The record buffer used for this example has two uses.  The 
          code in the program below uses only CASE 1 fields, CASE 2 is
          included as an example only.  }
        RecDef = RECORD	{ user defines field names and sizes }
          CASE integer OF	
            1 : (Dat1 : ARRAY [1..10] OF CHAR ;
                 Dat2 : integer ) ;
            2 : (Item1 : ARRAY [1..36] OF CHAR ;
                 Item2 : REAL ) ;
          END ;	{ User Defined Record }
       
       
        TwoWord	= ARRAY [1..2] OF integer ;	{ record number size }



      PRM Example of Creating an RMS Indexed File                  Page B-2



        KeyDef	= RECORD
          CASE integer OF	
            1 : ( KeyX : ARRAY [1..KeyXSize] OF CHAR) ;
            2 : ( KeyY : ARRAY [1..KeyYSize] OF CHAR) ;
            3 : ( RNum : TwoWord ) ;    { relative record cell no. }
          END ;
       
        RmsFileName	= ARRAY [1..NameSize] OF CHAR ;	
        RmsStatus	= ARRAY [1..2] OF integer ;	
       
        OrgTypes	= (SEQ,REL,IDX) ;	
        AllowTypes	= (Share,NoShare) ;      { what others can do }
        AccessTypes	= (PBoth,PRead,PWrite) ; { what you can do }
        FormType = (FFIX,FVAR,FSTREAM) ;	{ record format type }
       
        RmsFileDesc	= RECORD
          { -- Use with PRMOPE to define an existing file to be opened  -- }
          Org		: OrgTypes ;	{ spec. file type, no default }
          FileName	: RmsFileName ;	{ full spec. of rms file }
          LogChan	: integer ;	{ spec. ch. n, no def. }
          Allow	: AllowTypes ;	{ what others may do }
          Access	: AccessTypes ;	{ what you may do }
          RecordSize  : INTEGER ;	{ spec. max. file rec. sz }
          Windows	: INTEGER ;	{ no. of ret. windows }
       
          { enable the following options with a capital "Y" }
          DeferWrite	: CHAR ;	{ IDX, defer write }
          Unlock    	: CHAR ;  	{ unlock if locked }
          ObeyFill	: CHAR ;	{ obey bucket fill numbers }
          MassInsert	: CHAR ;	{ ref. rms-11 ref. man. }
          FileEnd	: CHAR ;	{ SEQ only, stream to EOF }
       
          { file creation fields }
          RecForm	: FormType ;	{ rec. format }
          Allocation  : TwoWord ;	{ no. blocks allocated to file }
          BucketSize	: integer ;	{ data bucket size }
          ExtQua	: integer ;	{ no. blks dynamic extend file }
          { Enable following with capital "Y" }
          Contiguous	: CHAR ;	{ create a contiguous file }
          Temporary	: char ;	{ delete the file when closed }
       
          workspace	: Array [1..160] of char ; 
        END ;	{ RmsFileDesc Record }
       
       
        SearchTypes	= (EQ,GT,GE,RFA,NEX,REC) ; 
        ThreeWord	= ARRAY [1..3] OF Integer ;	{ for RFA's }
        RecOps	= (GET,FIND,PUT,UPDATE) ;
       
        StoRecord = RECORD
            { USE with PRMSTO, Input to PUT and UPDATE }
            RecSize	: integer ;	{ INPUT - spec. rec. buffer 
                                        data to be stored }



      PRM Example of Creating an RMS Indexed File                  Page B-3



            RFAOut	: ThreeWord ;	{ OUTPUT - record RFA }
            Key	: KeyDef ;	{ INPUT - REL ONLY, rec.   }
          END ;	{ StoRecord Record }
       
          KType = (StrKey,IntKey) ;	{ string or unsigned integer }
        IdxKeyDesc = RECORD	{ used with prmkey to define keys }
                    { use prior to PrmCre of an indexed file type }
            KeyNum	: Integer ;	{ key of ref.   }
            KeyPos	: Integer ;	{ byte position of key in rec. }
            KeySiz	: Integer ;	{ size of the key defining }
            KeyTyp	: KType ;	{ string or unsigned integer }
            KeyDup	: char ;	{ 'Y' to allow duplicate keys }
            KeyChg	: char ;	{ 'Y' for key changes, alt. only }
            KeyNul	: char ;	{ null key value for alt. key }
          END ;	{ IdxKeyDesc }
       
       
       {************************************************************
                           END PRM CONST and TYPE
       *************************************************************}
       
      VAR
        FBuf		: RmsFileDesc ;	{ file creation buffer }
        RBuf		: RecDef ;	{ data record buffer }
        SBuf		: Storecord ;	{ storage desc. buffer }
        KBuf		: IdxKeyDesc ;	{ key description buffer }
        PrmStatus 	: RmsStatus ;   { status for all calls }
       
       
      {**********************************************************
       *                 START PRM PROCEDURE CALLS               *
       **********************************************************}
        
        
      { close the file }
      PROCEDURE PRMClo ( VAR Filebuf : RmsFileDesc ;	
                         VAR Status  : RmsStatus ) ; { STS and STV }
                         EXTERNAL ;
       
      PROCEDURE PrmCre ( VAR CreBuf : RmsFileDesc ;
                         VAR Status : RmsStatus ) ;
                         EXTERNAL ;
       
      { Define single key of indexed file, use in conj. with PrmCre }
      { Define keys in ascending order }
      PROCEDURE PRMKey (VAR Filebuf : RmsFileDesc ;
                        VAR KeyBuf : IdxKeyDesc ;
                        VAR Status  : RmsStatus ) ;{ Sts and Stv }
                         EXTERNAL ;
       
      { Store a record in the specified file }
      PROCEDURE PRMSto ( Operation   : RecOps ;	
                         VAR FileBuf : RmsFileDesc ;	



      PRM Example of Creating an RMS Indexed File                  Page B-4



                         VAR StoData : StoRecord ;	
                         VAR RecBuf  : RecDef ;	
                         VAR Status  : RmsStatus); { STS and STV }
                         EXTERNAL ;
       
      PROCEDURE RmsIni ; EXTERNAL ;
       
      {*********************************************************
       *                   BEGIN MAIN PROGRAM                  *
       *********************************************************}
        
      BEGIN
        RmsIni ;		{ required before any PRM call }
       
       { ***** BEGIN INDEXED KEY DEFINITIONS ***** }
       { linked list of XAB's created to define keys }
        WITH KBuf DO
          BEGIN
            KeyNum := 0 ;	{ KEY NUMBER 0, PRIMARY KEY }
            KeyPos := 0 ;
            KeySiz := 5 ;
          END ;
        PrmKey ( FBuf, KBuf, PrmStatus ) ;
        WITH KBuf DO
          BEGIN
            KeyNum := 1 ;	{ KEY NUMBER 1, ALTERNATE KEY }
            KeyPos := 3 ;
            KeySiz := 5 ;
          END ;
        PrmKey ( FBuf, KBuf, PrmStatus ) ;
        WITH KBuf DO
          BEGIN
            KeyNum := 2 ;	{ KEY NUMBER 2, ALTERNATE KEY }
            KeyPos := 4 ;
            KeySiz := 3 ;
          END ;
        PrmKey ( FBuf, KBuf, PrmStatus ) ;
        WITH KBuf DO
          BEGIN
            KeyNum := 3 ;	{ KEY NUMBER 3, ALTERNATE KEY }
            KeyPos := 8 ;
            KeySiz := 2 ;
          END ;
        PrmKey ( FBuf, KBuf, PrmStatus ) ;
       { ***** END INDEXED KEY DEFINITIONS ***** }
       
      { set-up the file parameters }
        WITH FBuf DO
          BEGIN
            Org := IDX ;		{ create an indexed file }
            FileName := 'cretst.IDX                    ' ;
            LogChan := 4 ;	
            RecordSize := 30 ;	



      PRM Example of Creating an RMS Indexed File                  Page B-5



            Allocation[1] := 10 ;	{ pre-allocate 10 blocks }
            Allocation[2] := 0 ;
            BucketSize := 2 ;
            Contiguous := 'Y' ;
          END ;	{ WITH FBuf } 
        PrmCre ( FBuf, PrmStatus ) ;	{ create the indexed file }
                       { DISPOSE of XAB's, return space to HEAP }
        writeln ( 'File created, sts=',prmstatus[1], '   
                   stv=',prmstatus[2] ) ;
       
        { store a single record }
        RBuf.Dat1 := 'file data ' ;
        RBuf.Dat2 := 64 ;
        SBuf.RecSize := 12 ;
        PrmSto ( PUT, FBuf, SBuf, RBuf, PrmStatus ) ;
        writeln ( 'Store data, sts=',prmstatus[1], 
                      '   stv=',prmstatus[2] ) ;
       
        PrmClo ( FBuf, PrmStatus ) ;
        writeln ( 'File closed, sts=',prmstatus[1],  
                    '   stv=',prmstatus[2] ) ;
      END.
       














                         APPENDIX C

              Command and Overlay Description Files




           Six logical unit numbers are provided by default for  each  task.
      Logical  channel  numbers  3 and 4 are available to the PRM user.  The
      other four are used by the  system  and  Pascal.   PRMExa  requires  3
      logical channel therefore UNITS=7 is specifed in the command file.
       
      File : PrmExaBld.Cmd
       
      PRMEXA/CP/FP,PRMEXA/-SP=PRMEXA/MP
      ;
      ; following possible only if RMS resident library is supported
      LIBR=RMSRES:RO:6
      ;
      ; refer to OMSI Pascal manual for detail on the following
      EXTSCT=$$HEAP:4000
      UNITS=7
      ;
      ; refer to the task builder manual Options description for details
       
      File : PrmExa.Odl
      ; REFER to RMS User's manual for detail on overlay files
      	.ROOT PRMEXA-RMS-PAS-RMSROT-RMSALL
      ;
      ;	pascal interface to PRM routines
      RMS:	.FCTR lb:[300,47]PRMPAS/LB
      ;
      ;	pascal libray
      PAS:	.FCTR lb:[300,41]PASLIB/LB
      ;
      ;	DEC supplied overlay structure for resident library
      @lb:[300,45]RMSRLX.ODL
      	.END















                         APPENDIX D

                         PRM Error Codes




           PRM-11 loads the RMS-11 completion code  in  a  two  word  buffer
      provided by the user for ALL PRM file and record operations.  The code
      loaded is compatible with the MACRO-11 STS and STV error code  values.
      Refer  to  Appendix B in the RMS-11 User's Guide for explantion of the
      RMS-11 error codes.

           If the PRM User incorrectly uses the PRM calls, PRM will generate
      an  error  code  unique  to the PRM interface.  The error code will be
      passed to the user in the STS field of the standard two  word  buffer.
      To avoid collision with standard error codes, PRM error codes start at
      -5000.

           The following table gives a brief explanation of the cause of the
      error.
       
      Symbolic  STS  STV  Description      
       
      PrINI   -5001   NA  A record operation was attempted on a
                          file that was not properly opened by 
                          PrmOpe or PrmKey.  Check proper open 
                          or create of a file before continuing 
                          with record ops. 
       
      PrRNE   -5002  Lch  An existing file was opened and the 
                          user program did not specify the 
                          correct file max. record size.  The 
                          logical channel no. of the file 
                          attempting to open is in word 2.  All 
                          record operations will be inhibited.
                          Use rms utility RMSDSP to determine 
                          actual record size and correct user 
                          recordsize.
       
      PrRsz  -5003  RecSz During a PrmRet call a record size 
                          must be specified so Prm knows the 
                          size of the record to be returned.  
                          The record size field is an input 
                          and output field therefore it must 
                          be loaded before EACH PrmRet.  A 



      PRM Error Codes                                              Page D-2



                          PrmRet rms failure will set the 
                          record size field to 0.  The record 
                          size specified by the user is 
                          returned in word 2.
       
      PrKY0   -5004  NA   During a PrmKey call the primary key 
                          must be specified first.  
       
      PrKNS   -5005  NA   During a PrmCre call a indexed file 
                          organization was specified and no 
                          primary key defined.  You must use 
                          PrmKey to define at least a primary 
                          key for indexed files.
       
      PrAsc	-5006  NA   Keys defined to PrmKey were defined 
                          in a non-ascending key order.