SEMAPHORE DIRECTIVES FOR RSX-11M-PLUS EXECUTIVE



	Version 02.3P		July 12,1982
	Last modification	Feb. 17,1983
 
	Harry Atherton
	University of Cincinnati Medical Center
	Department of Pediatrics, ML 541
	231 Bethesda Ave.
	Cincinnati, Ohio 45267
	Phone (513) 872-5341
 

     The files in this UIC implement binary semaphore
operations in the RSX-11M-PLUS executive.  This software has
been in use at our installation since RSX-11M V3.0, and it
is believed to be bug free.  If you have any problems,
comments, or suggestions I would like to hear them.  No
responsibility is assumed for the use or reliability of this
software.




SEMAPHORE DIRECTIVES FOR RSX-11M-PLUS EXECUTIVE       PAGE 2



     The following files implement the binary semaphore
P-operation and V-operation executive directives:

DRTBL.MOD   -- Adds the directives to the dispatch table.

DREIF.MOD   -- Adds call to cleanup routine on task exit.

SYSCM.MOD   -- Adds semaphore queues to executive data base.

DRSEM.MAC   -- Directive processing and exit cleanup
               routines.

SEMDIR.MAC  -- Macros that can be added to RSXMAC.SML to
               provide directive calls SEMP$S AND SEMV$S.

SEMCAL.MAC  -- FORTRAN callable subroutines provide
               directive calls SEMP and SEMV.  Object module
               should be added to your FORTRAN object
               library.

SEMTEST.FTN -- Small FORTRAN program to test and demonstrate
               use of semaphores.  The object module of
               SEMCAL.MAC must be available to the task
               builder.

SEMTEST2.FTN-- Small FORTRAN program to test for error
               return when SEMP is called twice.  The object
               module of SEMCAL.MAC must be available to the
               task builder.

               The following files are only relevant to a
               system using executive directive commons.

DIRCOM.ADD  and
DR2COM.ADD  -- Commands to be added to the corresponding TKB
               executive build files.

DIRCOM.DIF  and
DR2COM.DIF  and
DR211M.DIF  -- Listings of CMP output, showing the changes
               that are made to the various build files to
               include the semaphores in a system with
               executive directive commons.

     To add the semaphore directives a system generation
must be done.  To prepare for the SYSGEN copy files
DRTBL.MOD, DREIF.MOD, and SYSCM.MOD to [11,40] on the
executive source disk.  Also copy DRSEM.MAC to [11,10] on
the executive source disk.

     After applying any DEC supplied patches these
modifications are made.  The SLP correction files DRTBL.MOD,
DREIF.MOD, and SYSCM.MOD use ASCII string locators to insert



SEMAPHORE DIRECTIVES FOR RSX-11M-PLUS EXECUTIVE       PAGE 3



the additions to the program logic.  These files must be
applied AFTER any DEC patches.  Note that these files are
called .MOD instead of .COR to avoid confusing them with the
DEC files.

     Also watch out for file version numbers on the source
files if multiple SYSGENS are done on the same disk.  The
DEC correction files specify version 1 for input and version
2 for output.  If you are working with a virgin disk
everything will work right since the .MOD files do not
specify version numbers.  

     To have the module DRSEM assembled with the other
executive modules answer Y to the question:  "AE030 Do you
wish to pause to edit any files before assemblying ?" Then
edit the file [11,24]RSXASM.CMD.  Locate the line containing
DRSED.  It should look like:

[11,24]DRSED,listing=[1,1]EXEMC/ML,[11,10]RSXMC/PA:1,DRSED

Add a line exactly like it, except replace DRSED with DRSEM
(it occurrs three times in the line).  The module DRSEM will
be included in the executive object module library
automatically by SYSGEN.

     The executive TKB files must also be modified.  Answer
Y to the question:  "BE030 Do you want to pause to edit any
files before task-building ?" Different files are affected
depending on whether or not executive directive commons are
used.  If you are building the executive without executive
directive commons the directive modules are referenced in
file DIR.CMD.  Edit this file and locate the line containing
DREXP.  Add the following line after it:

[1,24]RSX11M/LB:DRSEM

If you are building the executive with directive commons the
module DRSEM should be placed in DR211M.  Three files must
be edited to accomplish this.  The TKB commands in
DR2COM.ADD and DIRCOM.ADD must be inserted in the
corresponding .CMD files before the final /.  References to
the DRSEM module must be added to files DR211M.CMD and
DR2COM.CMD.  Print the three .DIF files in this directory to
see what changes are made in the three corresponding .CMD
files.  After completing the editing the SYSGEN can proceed
normally from this point.

     When the SYSGEN is finished you can add the file
SEMDIR.MAC to [1,1]RSXMAC.SML so the macros SEMP$S and
SEMV$S will be available.  Also the file SEMCAL.MAC should
be assembled and the object module placed in
[1,1]SYSLIB.OLB, [1,1]ANSLIB.OLB, [1,1]F4POTS.OLB, and/or
[1,1]FOROTS.OLB so the FORTRAN subroutines SEMP and SEMV are



SEMAPHORE DIRECTIVES FOR RSX-11M-PLUS EXECUTIVE       PAGE 4



available.

     To demonstrate the functioning of the semaphores,
compile and build the programs SEMTEST.FTN and SEMTEST2.FTN.
By running multiple copies of SEMTEST from several terminals
you can see how the semaphore functions allow only one
program at a time to execute the "critical region" between
the P-operation and the V-operation.  The program SEMTEST2
works in a similar manner, but it calls SEMP twice and
prints the directive status from each directive call.  List
these programs to see what they do.

     The following pages describe the executive directives
in the format of the Executive Reference Manual.  Additional
information about semaphores is given in the paper
"Implementation and Application of Semaphores in RSX-11M"
presented at the Fall 1979 DECUS.  This appears in the
Proceedings of the Digital Equipment Computer Users Society
USA 1979 Fall.  Reprints are available from the author.


SEMP$S (only $S form supplied)

Semaphore P-operation

     The Semaphore P-operation instructs the executive to
place the issuing task on the specified semaphore list.  If
there is already a task on the list the issuing task is
suspended.  If no other task is on the list the issuing task
continues execution.

FORTRAN call:

CALL SEMP(number[,ids])

     number = Semaphore number

     ids    = Directive status

Macro call:

SEMP$S number[,error]

     number = Semaphore number

     error  = Error routine address

DSW Return Codes:

     IS.SPD -- Successful Completion (task was suspended)

     IS.SUC -- Successful completion (task was not
               suspended)

     IE.UPN -- Insufficient dynamic memory

     IE.ILU -- Semaphore number outside allowable range
               (range is 1-20;  upper limit is alterable at
               system generation time;  see module
               DRSEM.MAC)

     IE.ITS -- Program is already on the specified semaphore
               queue

     IE.ADP -- Part of DPB is out of the issuing task's
               address space

     IE.SDP -- DIC or DPB size is invalid

Notes:

     1.  If the task is suspended the suspend status bit is
         set;  see description of directive SPND$ for
         additional notes.


         SEMP$S (cont.)

     2.  Since the suspend bit is used the task may be
         resumed by the MCR command or the executive
         directive.  If this is done proper operation of the
         semaphore will be impossible.

     3.  There are two successful completion codes, IS.SPD =
         +2 and IS.SUC = +1.  If you are interested in
         knowing whether or not a program is actually
         suspended when it calls SEMP$S, the status returned
         will tell you.



SEMV$S (only $S form supplied)

Semaphore V-operation

     The Semaphore V-operation instructs the executive to
remove the issuing task from the head of the specified
semaphore list.  If any other tasks are on the list the one
at the head is resumed.  If the issuing task is not at the
head of the specified list no action is taken and status
code IE.ULN is returned.

FORTRAN call:

CALL SEMV(number[,ids])

     number = Semaphore number

     ids    = Directive status

Macro call:

SEMV$S number[,error]

     number = Semaphore number

     error  = Error routine address

DSW Return Codes:

     IS.SUC -- Successful completion

     IE.ULN -- Task was not at head of the specified list
               (Note 1)

     IE.ACT -- Next task on list was not active (Note 2)

     IE.ITS -- Next task on list was not suspended (Note 2)

     IE.ADP -- Part of DPB is out of issuing task's address
               space

     IE.SDP -- DIC or DPB size is invalid

Notes:

     1.  This will result if the task calls SEMV$S without
         having previously called SEMP$S with the same
         semaphore number.

     2.  This may be caused if a program using the
         semaphores is resumed by the MCR command or
         executive directive.

     3.  When a task exits the executive cleans up the
         semaphore lists.  If the exiting task has failed to
         do any required SEMV$S directives, they are
         simulated by the executive.