DEVELOPING AN RSX-11M ACP IN A HIGHER ORDER LANGUAGE
 
                                           Carl T. Mickelson
                                     Goodyear Aerospace Corporation
                                          1210 Massillon Road
                                           Akron, Ohio 44315
 
 
 
                                                ABSTRACT
 
                Developing  an  Ancillary  Control  Processor  (ACP)  in  a higher order
                language for  RSX-11M  is  not  difficult.   This  paper  describes  the
                development  of an ACP to control a complex permuting memory for a large
                scale parallel processor.  The central portions of the ACP  are  written
                in  FORTRAN.   The  program  was  originally  written  as an interactive
                program  to  aid  in  the  development  and  de-bug  cycle.   Once   the
                interactive  implementation  was  completed, the ACP form of the program
                was implemented using the same object library that was  used  to  create
                the   interactive   program.   The  paper  discusses  the  basic  design
                considerations  that  permitted  this  approach  to  be  successful.   A
                discussion of some of the implementation details, and how existing DECUS
                ACP documentation was used is also included. 
 
 
 
                                              INTRODUCTION
 
                In May 1983 Goodyear Aerospace Corporation (GAC) delivered the Massively
                Parallel  Processor (MPP) to the NASA Goddard Space Flight Center (GSFC)
                in Greenbelt, Maryland.  The  MPP  is  the  largest  and  most  powerful
                parallel processor ever built.  The central computational element in the
                MPP  is  a  square array of 16,384 bit-serial processing elements (PE's)
                with orthogonal nearest-neighbor connectivity  (figure  1).   Performing
                all  of its calculations using bit-serial techniques, the MPP is capable
                of performing  in  excess  of  6  billion  8-bit  additions  per  second
                (1,2,3,4). 
                
                Because  of  its parallel architecture, the "natural" memory access mode
                for the MPP PE's is to retrieve the same bit of each of 16K operands  in
                a   single   memory  cycle.   This  word-parallel  /  bit-serial  memory
                organization is in-consistent with the normal bit-parallel / word-serial
                memory organization of a conventional computer.  Since the data that  is
                processed  by  the  MPP  array  is generally provided by a conventional,
                word-serial host computer system, some way must be found to  re-organize
                or  "corner-turn"  the  data that will be processed in the array.  It is
                also highly desirable that this corner-turning  operation  be  performed
                "automatically",   without   the  requirement  to  execute  any  special
                re-formatting subroutines. 
                
                The solution to this problem is  provided  in  the  MPP  system  by  the
                inclusion  of  a  hardware buffer or staging memory inserted in the data
                path between the host computer and the array memory  (figure  2).   This
 
 
                                                   1                                    
 
 
 
 
 
 
 
 
 
 
                staging  memory,  which  can  be  expanded  to  64 megabytes, is used to
                permute data to be processed in the array unit as it is moved to or from
                the host computer into or out of the array memory.  The  staging  memory
                converts  the  bit-parallel  / word-serial host data organization to the
                word-parallel / bit-serial  organization  required  in  the  array  unit
                (figures  3  and  4).   Which of the 2**29 permutations performed by the
                stager is controlled by a set of  890  control  bytes  computed  from  a
                description of the data organization provided by the user. 
                
                The  purpose  of  this paper is to describe how the calculation of these
                control  bytes  is  accomplished  using  an  RSX-11M  Ancillary  Control
                Processor  (ACP)  and  to present some of the design considerations that
                were pertinent to the development of this ACP. 
                
                                        STAGER CONTROL SOFTWARE
                
                The use of an ACP in this application to provide support for the staging
                memory is justified for a number of reasons: 
                
                1. The calculation of the stager control constants is complex  and  best
                placed in a single program in the system.  This provides the consistency
                necessary  to  insure  proper  system  operation  for many different MPP
                application programs. 
                
                2. The ACP  mechanism  provides  the  capability  to  service  user  I/O
                requests  in  a  transparent manner.  All MPP I/O requests are routed to
                the MPP device driver.  It is the driver's responsibility to involve the
                staging memory ACP for those requests that require its support. 
                
                3. The ACP can be used to both create  and  to  manage  an  I/O  process
                involving  data  transfers  through the MPP staging memory.  The process
                creation or open function  is  used  to  compute  the  hardware  control
                parameters  required  to permute data as it is moved through the stager.
                These parameters are saved and subsequently used to program  the  stager
                hardware  whenever  a staging memory data transfer function is requested
                by an application program.  The  I/O  process  is  terminated,  and  the
                parameters  deleted  when  a close function is issued by the application
                program. 
                
                4. The ACP mechanism allows this software to be  developed  without  the
                restrictions  that  apply  to  an RSX-11M device driver.  As an ACP, the
                program has all the attributes of an RSX-11M task, and can be  overlayed
                to  support the complex computations necessary to produce the parameters
                needed to program the staging memory. 
                
                                       SOFTWARE DESIGN OBJECTIVES
                
                A  number  of  design  objectives  were  identified  early  in  the  ACP
                development  effort.   The  first  such  objective  was  to  develop the
                parameter  calculation  algorithm  in  the  form   of   an   interactive
                higher-order  language  program.  This type of development vehicle would
                provide the tool necessary to easily debug and check out the algorithm. 
                
 
 
                                                   2                                    
 
 
 
 
 
 
 
 
 
 
                A second objective was to use a single object library  to  support  both
                the interactive form of the parameter calculation algorithm and the ACP.
                Once the algorithm was developed and checked out, it was an objective to
                use  the  same  object  modules  to construct the staging memory ACP for
                on-line use with the MPP device driver.   Such  an  objective  could  be
                achieved   if   individual  modules  could  be  driven  from  either  an
                interactive  main  program  or  from  a  routine  providing  an  on-line
                interface to the user's I/O request (figure 5). 
                
                If  these  objectives could be achieved, both forms of the program could
                be supported from a single set  of  source  files,  easing  the  program
                maintenance  effort  and  eliminating  the  necessity  of re-writing the
                parameter calculation algorithm in assembly  language.   However,  these
                benefits are not achievable without considering the environment in which
                the ACP must execute. 
                
                All  interactive  FORTRAN  I/O must be eliminated in the ACP form of the
                program.  The I/O support required by FORTRAN  would  make  the  overall
                program  too large for an ACP.  Any error conditions detected by the ACP
                should be returned to the user program issuing the I/O request by way of
                the QIO I/O status block.  Error messages, issued directly to  the  user
                should be minimized. 
                
                The  ACP  must  fit into 12 Kwords of virtual address space, including a
                memory allocation bitmap for data buffers in the staging memory. 
                
                I/O processes  opened  by  the  ACP  must  maintain  all  the  necessary
                parameters  and information needed to program stager permutations at run
                time.  Multiple occurrences of such I/O processes should be able  to  be
                created  and maintained simultaneously.  Because of the possibility of a
                variable number of concurrently opened processes, the ACP data base  can
                not  be pre-sized.  Therefore, the parameters needed to maintain the I/O
                processes would be kept in Executive Pool. 
                
                Finally, to be easily used to support data transfers  to  and  from  the
                stager,  the  I/O  process  information  must be accessible to a FORTRAN
                subroutine in the ACP that programs and controls the stager hardware. 
                
                                        SOFTWARE DESIGN APPROACH
                
                The first step in developing the MPP staging memory control software was
                to identify all the parameters needed from  the  user  to  describe  the
                required  data  permutation  to  be  performed  in the hardware.  In the
                interactive form of the program, these parameters are read either from a
                data file or from the user's terminal.  In the ACP form of the  program,
                the same parameters are supplied in the user's data buffer identified in
                an "open" function QIO. 
                
                The  required  parameters, organized in a defined data structure for the
                "open" QIO, are used to initialize a FORTRAN common data  base  for  the
                hardware control parameter calculations.  The interactive program uses a
                prompt/response  subroutine to acquire the needed startup data.  The ACP
                uses a small assembly language subroutine to transfer the  initial  data
 
 
                                                   3                                    
 
 
 
 
 
 
 
 
 
 
                from the user's QIO buffer into the FORTRAN common data base. 
                
                The  ACP  version  of the program allocates a "window block" (similar in
                concept to the Files-11 ACP) in Executive Pool and uses  this  block  to
                collect  the  data  that  will  be needed later to move data through the
                staging memory.  The window block contains a pointer to a  second  block
                of pool used to store the computed hardware control parameters. 
                
                Both  the  interactive and the ACP versions of the program calculate the
                hardware control parameters required for  the  user's  data  permutation
                using  the  low  level  subroutines  that  are part of the common object
                module library.  These subroutines are implemented as FORTRAN  functions
                that  return  a status flag and/or error code in the event of a detected
                error condition. 
                
                The interactive program main module uses the error information to inform
                the user directly, via FORTRAN I/O statements, about the error  and  its
                cause.   The  ACP  version  of the program returns the error code to the
                user program that issued the QIO via the upper, device  dependent  byte,
                of  the  first  word  of  the  IOSB.   This design technique allowed all
                FORTRAN I/O requirements to be satisfied in a top-level routine so  that
                the low level routines were useable in both program versions. 
                
                Upon successful completion of the requested I/O process "open" function,
                the interactive program produces two output files.  The first contains a
                copy  of  the parameter calculation results in binary form.  The purpose
                of this file will be described later. 
                
                The second file is a listing of the  calculation  results  that  can  be
                interpreted  by  the user to determine the memory packing efficiency and
                I/O transfer rate achievable for his specified permutation.   A  listing
                file  option  permits  the  binary data to be presented in its entirety.
                This feature was used during the  program  development  effort  to  help
                debug the parameter calculation algorithm. 
                
                The  ACP  program  version  simply  stores the results of the successful
                parameter calculation step in the data block  allocated  in  pool.   The
                final "open" QIO step performed in the ACP is to build a FORTRAN calling
                sequence  in the I/O process window block.  All the parameters necessary
                to properly move data through the  staging  memory  are  identified  and
                located  through  addresses  contained  in  this  calling  sequence.  By
                passing the address of the calling  sequence  contained  in  the  window
                blocks  of  different  I/O processes to a single FORTRAN subroutine, the
                staging memory can be made to  perform  any  previously  specified  data
                permutation  in response to a data transfer QIO request issued by a user
                program. 
                
                An alternate "open" function is  also  available  that  permits  a  user
                program  to  create  a  stager I/O process without need of executing the
                parameter calculation algorithm at  run  time.   This  alternate  "open"
                function  makes  use  of  the  binary  output  data file produced by the
                interactive program.  The user program issuing such  a  "fast-open"  QIO
                provides  a  data  buffer  to the ACP that contains a copy of the binary
 
 
                                                   4                                    
 
 
 
 
 
 
 
 
 
 
                data file specifying the desired permutation.  The ACP uses the data  to
                build  the  same pool data structures that are constructed by the "open"
                function described earlier.  Once these structures are  created,  it  is
                not possible to determine how a particular I/O process was created.  The
                data  structures  contained  in  Executive Pool are identical for either
                case. 
                
                                      ACP IMPLEMENTATION APPROACH
                
                After developing and debugging the interactive staging memory  parameter
                calculation  program according to the design objectives and restrictions
                outlined earlier, development of  the  ACP  version  was  started.   The
                sample  ACP  package  (5)  was  used  as  a  starting point.  The manual
                accompanying the prototype ACP is an excellent source of information  on
                how an ACP interfaces with the RSX-11M QIO mechanism. 
                
                The  specific  type of ACP used for this application is characterized in
                the ACP documentation as a user ACP.  This  ACP  type  was  selected  in
                order  to  avoid  making changes to either the RSX module DRQIO, the QIO
                directive processor, or to the MCR mount processor (MOU). 
                
                In order to support  the  ACP,  the  user  written  device  driver  that
                processes  I/O requests for the MPP performs all parameter checks on all
                I/O functions including those  that  will  be  dispatched  to  the  user
                written  ACP.   These  parameter  checks  include the re-mapping of data
                buffer addresses provided in QIO requests to the driver or the ACP.   In
                order  for a data transfer to be accomplished properly, the user program
                virtual buffer address must be  mapped  into  a  kernal  APR  6  virtual
                address,  with  relocation  bias,  before  the QIO is queued to the ACP.
                When the ACP processes such an I/O request, and  subsequently  routes  a
                data  transfer  QIO to the device driver, the buffer address provided in
                the QIO is actually the previously relocated address of the user program
                data buffer.  Because of this, the device driver, in its  QIO  parameter
                checking  code,  must  not  relocate  the  data buffer address in an ACP
                issued data transfer QIO. 
                
                RSX-11M, by its design, requires that an ACP must be "known" or  mounted
                to  a  device  in order that "virtual" I/O functions can be issued for a
                device.  This mounting operation is the system step that establishes the
                link between a particular device and the  ACP  that  supports  it.   The
                tasks  that perform this function are the enable (ENA) and disable (DIS)
                tasks provided in the sample ACP package.  These programs were  directly
                applicable to this ACP development effort with only minor changes in the
                default  ACP  name coded into the ENA source.  Reference 6 provides some
                patches that should be applied to these programs before their use. 
                
                The basic  interface  with  RSX-11M  was  provided  by  the  sample  ACP
                prototype.   This  module  serves as the ACP's main program.  The stager
                control parameter calculation algorithm  developed  in  the  interactive
                program  is used for I/O process creation in the ACP.  This algorithm is
                called whenever an "open" QIO is issued to the ACP.   The  window  block
                created  for each of these processes is linked to the second LUT word of
                the issuing task's logical unit table entry for the LUN assigned to  the
 
 
                                                   5                                    
 
 
 
 
 
 
 
 
 
 
                staging memory.  This link is then used to access I/O process parameters
                whenever  a data transfer function is issued to the ACP.  If such a link
                does not exist, the ACP returns  an  error;  no  I/O  process  has  been
                created. 
                
                The  ACP  is  implemented  as  an  overlaid  program,  written mostly in
                FORTRAN.  The overlay structure is divided  primarily  between  the  I/O
                process creation or open functions and the data transfer functions. 
                
                The  I/O  process  open  function  uses  an  assembly language module to
                transfer the user's process description parameters  from  the  QIO  data
                buffer.  These parameters are used to initialize the same FORTRAN common
                region  that is filled in via user dialog in the interactive development
                program.  The ACP  then  executes  the  hardware  parameter  calculation
                algorithm  to  fill  in  the I/O process window block.  Error conditions
                detected in the user's initial data are returned to the user program  as
                an ACP error code. 
                
                After  completing  the hardware parameter calculation algorithm, the ACP
                fills in a 14 element FORTRAN subroutine calling sequence in the process
                window block.  This calling  sequence  is  used  by  the  data  transfer
                function module to move data into and out of the staging memory. 
                
                Assembly  language  modules are used to allocate space in executive pool
                for the parameter buffers referenced in the process window block.  These
                routines are also used to create an I/O process from pre-computed,  user
                supplied  hardware parameters from a saved binary data file as described
                earlier. 
                
                A data transfer request causes the ACP to find  the  appropriate  window
                block  linked to the second LUT word of the user program's assigned LUN.
                The main ACP module then calls a FORTRAN subroutine  to  do  the  actual
                data transfer using the calling sequence in the selected window block. 
                
                Even  though  the  ACP is overlaid, a properly written user program will
                not suffer excessive I/O processing delays.  If  all  the  required  I/O
                processes  are  created  and  then  used  repetitively,  the ACP overlay
                structure will not need to be re-loaded between QIO requests. 
                
                Some special steps are performed at compile  and  task  build  times  to
                minimize  the  size of the ACP.  First, the FORTRAN language modules are
                complied with all traceback code supressed.   Second,  FORTRAN  run-time
                error  messages are limited only to an announcement of the runtime error
                number and the program counter where the error occurred.   This  limited
                error  report  is  produced  by  task  building  the ACP with the F4POTS
                library module $SHORT.  Finally, since the ACP is  primarily  a  FORTRAN
                program  that performs no FORTRAN I/O, certain of the F4POTS I/O support
                modules may be shortened by using selected module versions contained  in
                the  F4PNIO  library.  This library can be created in UIC [1,1] from the
                FORTRAN language distribution file F4PNIO.OBJ.  Details of  the  use  of
                these  modules  can be found in the FORTRAN 4 Plus, or FORTRAN 77 User's
                Guides. 
                
 
 
                                                   6                                    
 
 
 
 
 
 
 
 
 
 
                                     DEBUGGING AIDES AND SURPRISES
                
                Debugging an ACP has some interesting side-effects.  Since  an  ACP  has
                all  the  attributes of a task, it can be debugged using ODT as a "user"
                program.  Additionally, if the "debuggable" ACP is built  with  default,
                rather than an elevated, priority, the debugging effort can generally be
                accomplished  without  a  severe  impact  on  system  performance.   Two
                complications arose in debugging this particular ACP because the program
                was overlaid and it was written in FORTRAN, requiring the use of some of
                the FORTRAN run-time support routines. 
                
                The first complication was eased significantly  by  making  use  of  the
                information  contained in reference 7.  Knowing the techniques described
                in this article, it should have been easy to start up the ACP and  begin
                a  debugging  session.   Since  an ACP is not normally started up like a
                user task, but rather by a request directive (RQST$) issued by  the  ACP
                enable  task  (ENA),  the  ACP  normally  runs  with TT0: as its default
                terminal device.  If the ACP is going  to  be  debugged,  and  TT0:  and
                another  system  terminal  are  available,  it is best to start the user
                program that will be using the ACP on the second terminal and  use  TT0:
                to  enter  ODT  debug  commands.   If only one terminal is available, it
                should be TT0:.  Debugging efforts can be successful if care is taken in
                entering commands since the terminal is shared by both the user  program
                and ODT. 
                
                However,  attempting  to  debug  the  ACP with ODT proved to be somewhat
                challenging.  When the enable task (ENA) was used to initiate the ACP to
                be debugged, it seemed that the program would not execute.   If  started
                from a terminal with a RUN command, the ACP would properly prompt for an
                ODT command and would run correctly when started with the "G" command. 
                
                As  a  result  of  a  telephone  conversation  with Ralph Stamerjohn, at
                Monsanto, it was finally realized that the ACP, when started by the  ENA
                task,  was  running  with  its terminal set to the CO: device.  When the
                task was started, ODT would attempt to input a command from  CO:.   With
                the  console  logger  (COT...)  active,  the  read  request  received an
                end-of-file and the ACP exited!  If COT... was first  stopped  with  the
                command  SET  /NOCOLOG,  the  ACP  built with ODT executed properly when
                started with the ENA task.  Note that during  normal  system  operation,
                using  an ACP without ODT, if the ACP should abort, the console log will
                have a message containing information identifying the cause and location
                of the error. 
                
                The second check-out complication encountered in developing the ACP  was
                related  to  the  FORTRAN OTS interface.  The FORTRAN subroutine used by
                the ACP to move data through  the  staging  memory  has  three  optional
                variable length arrays passed to it when it is called with the parameter
                list  built  in the I/O process window block.  Certain permutations that
                have no need to use these arrays use an address value of -1 to  indicate
                that the parameters are not defined. 
                
                When  five  calls were made to this subroutine for permutations that did
                not use the optional parameters, the ACP would abort.  The  problem  was
 
 
                                                   7                                    
 
 
 
 
 
 
 
 
 
 
                traced to a FORTRAN OTS run-time check done on variable length passed to
                a  subroutine.   Since the address -1 is an illegal PDP-11 word address,
                the OTS would detect and count an array size error for each  unspecified
                array parameter upon entering the subroutine.  When the task error count
                was  exceeded, the ACP aborted.  The fix for this particular problem was
                to call the ERRSET subroutine during  ACP  initialization  to  turn  off
                error  logging and limit checking for this error condition.  In this way
                the ACP would continue to execute correctly for  permutations  that  did
                not require the optional parameters. 
                
                                          FURTHER INFORMATION
                
                Selected  modules  from  the  ACP, together with the manuscript for this
                paper are available on  the  RSX  Sig  Tape  for  the  Fall  1983  DECUS
                Symposium.   The  modules included on the tape are limited only to those
                top-level routines  that  characterize  both  the  interactive  and  ACP
                program  forms.   The  missing modules are limited to those that perform
                the actual stager hardware parameter calculations.   These  modules  are
                peculiar  to  the ACP developed for the MPP.  They provide no additional
                specific insights into the design of an ACP for implementation  using  a
                higher order language. 
                
                                               REFERENCES
                
                1.  Batcher,  Kenneth  E.,  "Massively Parallel Processor (MPP) System",
                AIAA Computers in Aerospace Conference II, October 1979
                2. Tsoras, John, "The Massively Parallel Processor (MPP), Innovation  in
                High  Speed  Processors",  AIAA  Computers  in Aerospace Conference III,
                October 1981
                3. Gilmore, Paul  A.,  "The  Computer  MPP",  International  Society  of
                Photogrammetry  and  Remote  Sensing  Commission  II Symposium, August -
                September 1982
                4. Burkley, John T. and Mickelson, Carl T., "MPP:  A  Case  Study  of  a
                Highly  Parallel  System",  AIAA  Computers  in Aerospace Conference IV,
                October 1983
                5. Stamerjohn, Ralph, "Up Your ACP" (et al), DECUS Spring 1980 Symposium
                RSX SIG Tape, UIC=[346,100]
                6.  Stamerjohn,  Ralph,  "Bug  Fixes  for   Sample   ACP",   DECUS   RSX
                Multi-Tasker, Vol 16, #2, August 1982
                7.  Johnson,  Kenneth,  "Using  ODT  in  Overlaid  Programs",  DECUS RSX
                Multi-Tasker, Vol 13, #2, August 1980
                8. "MPP System User's Guide", Goodyear Aerospace Corporation,  GER-1714,
                April 1983
                
                                            FIGURE CAPTIONS
                
                                       Figure 1 - MPP Array Unit
                
                                  Figure 2 - MPP System Block Diagram
                
                                     Figure 3 - MPP Staging Memory
                
                                 Figure 4 - Stager Reformatting Example
 
 
                                                   8                                    
 
 
 
 
 
 
 
 
 
 
                
                                  Figure 5 - Stager Software Structure
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                                   9