CROSS

                    Ted Hess, Digital Equipment Corporation
                                    author

                Joseph M. Newcomer, Carnegie-Mellon University
                                 documentation












                               19 February 1981

  The  material  used  in  this  specification,  including  but  not limited to
construction times and operating speeds, is for  informational  purposes  only.
All  such material is subject to change without notice.  Consequently DEC makes
no claim and shall not be liable for its accuracy.





  This document describes the operational procedures for  CROSS,  an  assembler
which  operates  on  the  DECsystem-10/20  systems, translating source code for
6502, 6800, 6805, 6809, 8080, 8085, MCS-48,  Z80,  1802,  3870/F8[future],  and
8008 micro-processors into binary files suitable for absolute load.

  All of the appendices to this manual and the index were constructed by Joseph
M. Newcomer,  Carnegie-Mellon  University  Computer  Science  Department.   The
information for the appendix on object  formats  is  derived  from  information
contributed  by  Ted  Hess, but the current editor takes responsibility for any
inaccuracies which may have crept in during the transcription.

  Additional work has been done on CROSS by Mark L. Sproul and Mel  J. Pleasant
at Rutgers University.

                      CROSS-Microcomputer cross assembler                     1


1. Introduction
  CROSS  is  an  assembler  which operates on the DECsystem-10/20 and assembles
code for many currently available micro-processors. With the exception  of  the
variations  listed  in this manual, CROSS implements the features of the PDP-11
macro  assembler  for  RSX-11D.    No  attempt  was  made  to  provide   source
compatibility  between  CROSS  and  other micro- processor assemblers.  Rather,
CROSS has been designed to provide consistent, powerful features for all of the
mnemonics associated with each micro-processor.

  Numerous people have worked on CROSS over the years; appropriate credits  are
recorded in the change log of the source.

  While CROSS is designed to be language compatible with the MACRO-11 language,
its   PDP-10  operating  environment  necessitates  a  PDP-10  style  operating
procedure.

  Expression evaluation has been updated to provide the following features:

   - Default radix is decimal.

   - @<expr> indicates octal radix, same as to ^O<expr>

   - %<expr> indicates binary (6502/6800/6809 only), same as to ^B<expr>

   - %nn indicates register value nn (all others)

   - $<expr> indicates hexadecimal radix

   - ^H<expr> indicates hexadecimal radix

   - <expr>^ indicates that the evaluated expression is to be  divided  by
     256. (high byte)

   - <expr>\ indicates that the evaluated expression is to be taken modulo
     256 (low byte).

  The  assembler  makes  two  passes over the source, outputting the binary and
listing files during pass two and appending a symbol or cross  reference  table
to  the  listing file.  PDP-10 memory is dynamically allocated for large symbol
table storage and macro storage.












                                                                   Introduction

                      CROSS-Microcomputer cross assembler                     2


2. Syntax differences
  The  syntax  of  CROSS  is more compatible with that of MACRO-11 than that of
most manufacturer's assemblers.  This means  that  you  will  not  be  able  to
compile  straight  8080,  Z80, 6502 or 6800 code with this assembler.  However,
the transliterations are reasonably straightforward and are described for  each
machine  in  the  appendices.  In general, you must specify registers with a %-
directive.

  The machine which differs most from the manufacturer's  specification  of  an
assembler  syntax  is  the Zilog Z80.  This is because CROSS implements the Z80
syntax as a superset of the 8080 syntax.   Consequently,  the  syntax  of  most
operations  follows  that  of  the  8080.    In  addition,  some  Z80 mnemonics
conflicted with 8080 mnemonics; the Z80 has been assigned new  mnemonics  where
these  conflicts  existed.  Any Z80 operation which has no 8080 counterpart has
also been assigned a mnemonic;  some  correspond  to  the  Zilog  specification
(wherever  this was possible) and most do not.  Consequently, a complete cross-
reference between the Zilog syntax  and  the  CROSS  transliteration  has  been
provided.


































                                                             Syntax differences

                      CROSS-Microcomputer cross assembler                     3


3. Operating procedures

3.1. Loading CROSS
  CROSS is run by typing the monitor command:

    @CROSS                 ;tops20
    .R CROSS                ;tops10

3.2. Initial dialogue
  When  the assembler is ready to accept the user's command string, it types an
asterisk.  The user must now type the command string on the same line.

  The general form of the command string is:

                binary output, listing output = source input(s)

  In addition, the command(s) may be stored in a file (default extension  .CCL)
and read in by specifying:  

    @filename

  Each input/output specification consists of the group:

                    dev:filnam.Ext[proj.,prog.]/switch:arg

   - dev is:

     DSK             for disk

     PTR             for paper tape reader

     PTP             for high speed punch

     TTY             for the user's terminal

     LPT             for a queued line printer

   - If not specified, the device is assumed to be the disk.  Other system
     devices may also be used, depending upon the system configuation.

   - filnam is the file name of the appropriate file.

   - ext  is  the file name extension for that file.  If is not specified,
     the assumptions are:

     binary string:  .BIN (absolute)

     listing string: .LST

     source string:

                     .M05            Motorola 6805
                                                                      Operation

                      CROSS-Microcomputer cross assembler                     4


                     .M48            Intel MCS-48 family

                     .M65            MOS Technology/Synertek/Rockwell 6502

                     .M68            Motorola 6800

                     .M69            Motorola 6809 family

                     .M80            8080/Z80/8085

                     .M88            8008, 8080 mnemonics

                     .M08            8008 , Intel mnemonics

                     .M18            CPD1802, COSMAC

                     .MF8            Fairchild F8/Mostek 3870 [future]

   - [proj.,prog.]  is the project-programmer number assigned for the disk
     area to be used.  If not specified, the user's local area is assumed.
     Once specified, the number pair becomes the  new  default  assumption
     for  the following files. (Use translate command on TOPS20).  At CMU,
     the CMU PPN format is accepted.

   - Switches are specified by preceding  each  with  a  slash  character.
     Switch  arguments  are  preceded  by colons.  In addition to explicit
     specifications of the switches, a default  set  of  switches  may  be
     specified with a SWITCH.INI file (chapter 6, page 13).

     /M05            source is Motorola 6805 code

     /M48            source is Intel MCS-48 code

     /M65            source is 6502 code

     /M68            source is Motorola 6800 code

     /M69            source is Motorola 6809 code

     /M80            source is Intel 8080, Intel 8085 or Zilog Z80 code

     /M88            source is 8008 using 8080 compatible mnemonics

     /M08            source is Intel 8008 original Intel mnemonics

     /M18            source is 1802 code (RCA COSMAC)

     /MF8            source is Fairchild F8/Mostek 3870 [future]

     /LI             simulate .LIST directive (see chapter 4).

     /NL             simulate .NLIST directive (see chapter 4).
                                                                      Operation

                      CROSS-Microcomputer cross assembler                     5


     /EN             simulate .ENABL directive (see chapter 5).

     /DS             simulate .DSABL directive (see chapter 5).

     /CRF            append  cross  reference  table  to the listing files
                     (see chapter 4).

     /PTP            binary output is ASCII coded hex.  This switch  takes
                     an  optional format type as a parameter, as /PTP:fmt.
                     The format types are:

                     COS             Uses RCA COSMAC format  (see  section
                                     XV.1.1) 

                     INT             Uses   Intel   Intellec  (CP/M  .HEX)
                                     format.  

                     KIM             Uses MOS Technology format with start
                                     address in the last record (this  was
                                     the  default  CROSS format for a long
                                     time).  

                     MOS             Uses  MOS  Technology   format   with
                                     record count in last record.  

                     MOT             Uses  Motorola  Exorcisor  format (S1
                                     and S9 records) 

                     If no argument is specified, the format is based upon
                     the  language  input  type  determined  by  the  file
                     extension:

                     Extension                  PTP Format
                     .M65                       MOS
                     .M68,.M69                  MOT
                     .M80,.M08,.M88,.M48        INT
                     .M18                       COS
                     .MF8                       KIM (future)

     /N              suppress  error  messages and expanded summary to the
                     terminal.

     /OCT            listing format in octal - hex is default

     /I              output binary in image mode (one byte per 36 bit PDP-
                     10 word). This switch must be used to  copy  directly
                     to paper tape.

     /P              pack binary output.  This is the default case and the
                     switch is not needed.

     /CDR            simulate   card  reader  input.    This  is  actually
                                                                      Operation

                      CROSS-Microcomputer cross assembler                     6


                     independent  of  the physical input device but causes
                     the assembler to ignore all characters  on  a  column
                     after the 72nd.

     /SOL            sequence output lines (see chapter 4).

     /GNS            generate new source (see chapter 4).

     /NSQ            suppress listing of PDP-10 style seq. Numbers.

     /EQ             equate  the  following  symbols  to  zero.  This is a
                     method for introducing conditional arguments  without
                     creating special parameter tapes.  "/EQ:sym1:sym2" is
                     the  equivalent of the source statements "sym1=0" and
                     "sym2=0".

     /LEN            set the page length for the output listing.

     /WID            set the page width for the output listing.

































                                                                      Operation

                      CROSS-Microcomputer cross assembler                     7


4. Listing control
  CROSS has two categories of listing controls:  MACRO-11 compatible, which may
be  specified  either  in  source  statements  or  in the command string, and a
superset which is limited to the command string.

4.1. Source statement listing control
  Listings are controlled at source statement level through   the  use  of  the
.LIST  and  .NLIST  directives.    These are complementary in that any function
which can be enabled by a .LIST can  be  disabled  by  a  .NLIST.    To  reduce
redundancy,  the following descriptions will emphasize the .LIST while implying
the .NLIST complement.

  The following are the allowable arguments for the .LIST directive along  with
the default settings (li for .LIST and nl for .NLIST):

  The  first  group  controls  intra-line listing.  Suppression of any of these
will cause the assembler to utilize the space by moving the  remainder  of  the
line over.

SEQ             list  the sequence numbers.  These numbers represent the source
                line  numbers  and  are  replaced  by  the  nesting  level   in
                parentheses for generated lines (macros, etc.).

LOC             list the value of the location counter.

BIN             list the binary code generated by the assembler.

SRC             list  the  source  statement.    This is included primarily for
                completeness.

COM             list the comment field.

BEX             list binary code which requires more  than  one  listing  line.
                suppression  of  this  is  particularly  useful in reducing the
                length of listing required for long .ASCII strings.

  The following arguments pertain to entire statements:

MB              list macro binary and call only - no source

MD              list macro definitions.

MC              list macro calls.

ME-nl           list macro expansions.  The default causes the expansion to  be
                suppressed  in the interest of supply economy.  ME controls all
                generated text (.MACROs, .REPTs, and .IRPs).

                Caution - due to their dual nature, .REPTs  and  .IRPs  qualify
                both  as  definitions  and  calls.  CROSS treats MD and MC as a
                pair in these cases, suppressing the listing if either is set.

                                                                   .LIST/.NLIST

                      CROSS-Microcomputer cross assembler                     8


CND             list conditionals.  Suppression causes unsatisfied conditionals
                and all conditional directives (whether satisfied or not) to be
                not listed.

SYM             append a symbol table to the listing file.

TTM             list  in  terminal  format  (one  column  of  binary to a line,
                truncation after 72 columns).  Default setting is determined by
                the output device specified:  enabled if the physical device is
                TTY: and disabled (line printer mode) in all other cases.

TOC-nl          list a table of contents during pass one.  This consists of the
                .SBTTL directives being listed at the beginning of the  listing
                file.    Each  line consists of the line number and all text to
                the right of the .SBTTL directive.

LD-nl           list  listing  directives.    Specifically,  this  causes   all
                .LIST/.NLIST  directives  which have no arguments to be listed.
                its primary use is in debugging listing control.

  .LIST and .NLIST directives with no arguments perform an over- ride function.
They control a listing  "level"  which  is  decremented  for  each  .NLIST  and
incremented for each .LIST.  The level count is used as a three way switch:

   1. Zero (initial condition):  no special action.

   2. Less  than  zero:    unconditionally suppress the listing except for
      lines containing errors.

   3. Greater than zero:  list unconditionally.

  .LIST/.NLIST are normally paired to return the level  count  to  zero.    the
.NLIST/.LIST  sequence  is  used  to suppress a range which is normally listed,
while the .LIST/.NLIST sequence is used to over-ride a range which is  normally
suppressed,  such  as  in  a  macro  expansion.    The level count allows macro
expansions to use the listing control and return it to its previous state.

4.2. Command string equivalents
  The command string contains the equivalent of all the above .LIST and  .NLIST
functions as well as some that are not available at source level.  Indeed, many
of  the  source level arguments are of primary interest at command string level
but can be used in the source to modify default settings.

  The command  string  equivalents  of  .LIST  and  .NLIST  are  /LI  and  /NL,
respectively.    Arguments  are  specified by preceding them with colons.  Thus
/NL:bex:cnd is the equivalent of .NLIST CND,BEX.

  In all cases, command string switches override their source level equivalents
(as well  as  previous  occurrences  in  the  command  string).    Effectively,
specification of a function in a command string will cause all its source level
equivalents  (and  their  complements) to be ignored.  i.e. /LI:me would enable
the listing of macro expansions and cause all ".LIST/.NLIST ME"  directives  to
                                                                   .LIST/.NLIST

                      CROSS-Microcomputer cross assembler                     9


be ignored.

  /LI  (no  arguments) causes everything to be listed, while /NL suppresses the
listing of all but error lines, the  symbol  table,  and  the  cross  reference
tables.

4.3. Other listing controls
  The  following swithces are specified in output side of the command string by
preceding the mnemonic by a slash:

/OCT            list in octal - default is hex

/N              suppress error messages to the terminal (unless it is also  the
                listing device).

/CRF            append  a  cross  reference  table  to the listing file.  CROSS
                accomplishes this in the following manner:

                   1. The listing file is  generated  in  the  normal  way
                      during  pass  two,  using  the name specified by the
                      user.

                   2. Simultaneously, a temporary file (xxxCRF.TMP,  where
                      xxx  is  the  job number) is created.  This contains
                      encoded cref information.

                   3. At the end of pass two, the temporary file  is  read
                      and  the  cref  information  is  integrated into the
                      symbol table.

                   4. The references are appended to the listing file.  if
                      insufficient core was available to build the  table,
                      the   process   is  repeated.    When  through,  the
                      temporary file is deleted.

                The cross reference table format is as follows:

                   1. The symbol itself.

                   2. Its  symbol  table  value,  unless  .NLIST sym   was
                      specified.    Therefore  the  symbol table itself is
                      always pre-empted.

                   3. All references to the symbol, except  that  no  more
                      than  one  reference  to a given source line will be
                      listed.  symbols in generated text always  refer  to
                      the previous source line.

                   4. Defining occurrences are flagged with a "#".

                   5. Destructive  references  are  flagged  with  a  "*".
                      These are defined to be all symbols  encountered  in
                                                                   .LIST/.NLIST

                      CROSS-Microcomputer cross assembler                    10


                      op-code fields which store into a memory location or
                      a register.

                   6. As  many  references  per  listing line as possible,
                      depending upon the "ttm" mode, are used.   This  can
                      be increased by suppressing "sym".

/SOL            Sequence output lines.  Listings are normally source oriented:

                   1. Sequence numbers reflect the source line number.

                   2. Macro  expansion  lines have their nesting level, in
                      parentheses, in the sequence number field.

                   3. Lines containing nothing but a  form  feed  are  not
                      listed   but   cause   the  sequence  number  to  be
                      incremented.

                   4. Page   numbers   reflect   physical   input    pages
                      (incremented  only  upon  encountering a form feed).
                      Pages forced by the assembler have a -n  to  reflect
                      an  extension  page.    i.e.    If the assembler had
                      encountered 3  form  feeds  and  was  on  its  third
                      listing  page  since the last one, it would be "page
                      4-2".

                when /SOL is specified, listings are output oriented:

                   1. Listed lines have consecutive  numbers,  except  for
                      binary extensions.

                   2. Page numbers reflect the number of pages listed.

/GNS            Generate a new source.  This causes the listing file to take on
                the appearance of a source file.  specifically, it:

                   1. Suppresses  the  listing  of  headers,  error flags,
                      summary blocks, and any other output over which  the
                      user otherwise would have no control.

                   2. Simulates a /NL:seq:loc:bin:bex:me.

                   3. therefore,  by itself, it recreates the source file.
                      Normal  usage  would  have  supplementary   switches
                      following  it.    i.e.  /gns/nl:md:mc  /li:me  would
                      replace macros, repeats, and irps by their generated
                      code,  /gns/nl:cnd  would  purge  conditionals,  and
                      /gns/li:seq  would be an expensive way of creating a
                      sequence numbered listing of the source file.

/LEN:num        Sets the page length to the specified number.  This allows  the
                user  to  take  advantage  of  longer  page  formats  for  some
                                                                   .LIST/.NLIST

                      CROSS-Microcomputer cross assembler                    11


                printers, or to produce listings suitable for viewing a page at
                a  time on a video terminal.  At CMU, the default length is 80,
                for the Dover using SAILA8.  The normal default is 58.

/WID:num        Sets the page width to the specified number.  This  allows  the
                user   to   take  advantage  of  wider  page  formats,  or  get
                presentable listings on devices which  have  narrower  margins,
                such as home microcomputer printers.  At CMU, the default width
                is 120, for the Dover using SAILA8.  The normal default is 132.











































                                                                   .LIST/.NLIST

                      CROSS-Microcomputer cross assembler                    12


5. Enable/Disable control
  As  an  alternative  to  the  proliferation  of  directives,  CROSS  uses one
complementary pair, .ENABL/.DSABL, with arguments.  Their       command  string
equivalents  are  /EN  and  /DS.    The relationship between command string and
source statement specification, as well as their argument specification, is the
same as in .LIST/.NLIST.

M85             allow 8085 opcodes (RIM/SIM) in .M80 files

Z80             allow Z80 opcodes in .M80 files

FPT             floating point  truncation.    ".ENABL FPT"  is  equivalent  to
                ".TRUNC" while ".DSABL FPT" is equivalent to ".ROUND".

ABS             absolute assembly

AMA             absolute memory addressing

NPP             ".ENABL NPP"  causes suppression of the output of the following
                code, while ".DSABL NPP" causes its resumption.

ERF             error flags can  be  selectively  suppressed  (or  enabled)  by
                specifying   ERF,  directly  followed  by  the  selected  error
                characters.  "/ds:ERFzm" would cause "m" and "z" errors  to  be
                ignored,  "/ds:ERF"  would  cause all errors to be ignored, and
                "/en:ERFa"  would  cause"a"  flags  (argument  errors)  to   be
                flagged.

LC              lower  case  to upper case translation of input; the default is
                .ENABL LC so listings contain output in the same case as it was
                input.

LSB             local symbol block

TIM             timing information - causes number of states to  be  output  on
                the  listing.  Alas, for most machines this data is not entered
                in the internal tables.

REG             default register names













                                                                  .ENABL/.DSABL

                      CROSS-Microcomputer cross assembler                    13


6. User-defined switch defaults
  CROSS  is  capable  of  accepting user-defined switch defaults.  Any switches
that are valid in a command string may be specified in a  special  file  called
SWITCH.INI.    When  CROSS  is  run,  it  will look for this file in the user's
directory. At CMU, the logical device HOM: is checked, and if a SWITCH.INI file
is found there, it will be used instead of the one on the aliased or  connected
          1
directory.  If  the  file  is  not found, then  standard  defaults (as  defined
elsewhere in this document) are assumed.  If SWITCH.INI is found, but no  CROSS
switches are found, default settings are assumed.

  To  specify  defaults,  use the editor of your choice to create a file called
SWITCH.INI.  This file must contain a line of the following format:

    CROSS/switch1/switch2...../switchn

  continuation lines are permitted.  Specifically, a line containing a terminal
hyphen is assumed to be followed by a continuation line.

  Of course CROSS does not consider the hyphen to be a part of any switch.

  Note that this feature is a subset of the facility offered normally by use of
SWITCH.INI files.
























               

  1
   At CMU on TOPS-20, the logical device HOM: can be  assigned  to  the  user's
login directory by the LOGIN.CMD file.
                                                                     SWITCH.INI

                      CROSS-Microcomputer cross assembler                    14


7. Macro libraries
  Macro libraries are used by the .MCALL directive.  As in Macro-11, the format
is:  

        .MCall arg1,arg2,...

where  the  arguments are macro names required for the program.  However, CROSS
recognizes that users may  wish  to  have  different  libraries  for  different
machines,  but  a single user may be using CROSS for several different machines
at the same time.  Therefore, instead of the simple  rule  that  SYSMAC.SML  is
used,  if  it  exists,  and  then  trying  SYS:SYSMAC.SML, CROSS uses language-
dependent libraries.  The extension of the library is the appropriate extension
for the language being compiled. Thus, if you have a file whose extension,  for
reasons known only to yourself, is ".M80" but which contains 6809 code, and you
have  overridden  the  default language selection with a /M69 switch, the macro
library will have extension ".M69".  The extensions are the default  extensions
discussed on page 3, and in the rules below are indicated by language.

  The search rules are thus:

    DSK:SYSMAC.SML
    DSK:SYSMAC.language
    SYS:SYSMAC.SML
    SYS:SYSMAC.language




























                                                                     SWITCH.INI

                      CROSS-Microcomputer cross assembler                    15


I. General notation
  Each section of an appendix describes one aspect of a given machine

I.1. Machine State
  This  section defines the registers or other status of the machine, including
condition code bits.  This status is referred to in  the  descriptions  of  the
instructions,  and  thus  may  include  status  or  registers  which  cannot be
specified in the syntax to CROSS.

I.2. Notation
  This  section  describes  the  notation  used  in  the  description  of   the
operations.  For example, a set of instructions might all use registers R1, P2,
C3  and  D4, or immediate data.  This collection might be called src-opnd, thus
reducing the number of cases which need to appear in the opcode  list.    These
names, and other notations, appear here.

I.3. Syntax
  Here,  the actual CROSS representation details, particularly when they differ
from those of the manufacturer's standard assembler, are discussed.

  The names of locations, registers, operands, etc. which correspond to machine
state which can be referred to are given here.

I.4. Opcodes
  Here, the complete list of mnemonics  are  given.    This  list,  the  syntax
section, and the notation section should allow one to write actual CROSS code.

  The comments in the opcode list describe the operation; while not intended to
replace  the  manufacturer's or other reference manual, they do provide a quick
check on what is happening.

  The semantics are expressed either as comments, or as fragments  of  code  in
the Bliss language.  In Bliss, the "." operator means "contents of", and a name
stands for its "address".  Thus, a description such as 

    A = .A + 1

means that register (or location) A gets the contents of register (or location)
A plus 1.

  Bit fields are indicated by <> pairs, of the form <position,size>.  Thus, 

    .A<1,4>

means  the contents of the register (or location) named by A<1,4>, i.e., bits 1
thru 5.  Bit 0 is the low order bit.

  Multibyte and other  complex  fields  are  indicated  by  catenation,  the  |
operator; thus, the HL register pair of the 8080 is indicated by %H|%L.

  Boolean  truth  and falsehood is determined by the value of the low-order bit
of the expression used as the boolean; thus 0, 2, 4, 6, etc.  are  all  "false"
                                                                     SWITCH.INI

                      CROSS-Microcomputer cross assembler                    16


values.

  The  following  table  gives the operation names used for the descriptions of
the instructions and explanations of their meanings.

and             bitwise and
ash             arithmetic shift, positive values shift left, negative values
                shift right
geq             greater than or equal, signed, two's complement
gequ            greater than or equal, unsigned
gtr             greater than, signed, two's complement
gtru            greater than, unsigned
leq             less than or equal, signed, two's complement
lequ            less than or equal, unsigned
lss             less than, signed, two's complement
lsh             logical shift, positive values shift left, negative values
                shift right.
lssu            less than, unsigned, two's complement
not             bitwise complement
or              bitwise or
rot             rotate, positive values are rotate left, negative values are
                rotate right
xor             bitwise exclusive or
+               two's complement add
-               two's complement subtract
*               two's complement multiply
<=>             swap; the contents of the two locations named are swapped.

























                                                                     SWITCH.INI

                      CROSS-Microcomputer cross assembler                    17


II. 8080 syntax

II.1. Machine State
  The registers for the 8080 are defined as:

   - %A - the accumulator
   - %B - register B
   - %C - register C
   - %D - register D
   - %H - register H, high-order memory reference register
   - %L - register L, low-order memory reference register
   - %SP - the stack pointer register
   - %PSW - the processor status, or F register

  Register  pairs  are  written  in  the  description  of  each  instruction by
concatenating two names with a vertical bar, e.g., %H|%L is the 16-bit value in
the HL register pair.  Parentheses are  sometimes  added  for  visual  clarity,
e.g., ".(%H|%L)".  The flags in the status register are represented by:

   - c - the carry bit
   - p - the parity bit.  True if the last operation had odd parity, false
     if even parity.
   - z - the zero bit.  True if the last operation had a zero result.
   - s - the sign bit.  True if the last operation had a negative result.
   - ie - the interrupt enable flag.

  In each description of an instruction that alters the condition codes, either
an  explicit  assignment  is  written  (e.g., "c=0") or the condition codes are
listed in curly brackets.  In this case,  it  is  implied  that  c  is  set  to
indicate  carry  or  borrow (arithmentic operations), z is set if the result is
zero, s is set if the result is negative, and p is set if the parity is even.

II.2. Notation
  To reduce the size of the description, several notational conventions will be
established for desribing the operands:

   - i - represents an immediate operand which is 8 bits wide.

   - m - represents a memory operand which is 16 bits wide.

   - M - represents an implied memory operand addressed  by  the  register
     pair %H|%L.

   - MEM - represents all of addressible memory.

   - DEV - represents all addressible devices.

   - v - a special 3-bit value used for the RST instruction

   - opnd  -  a  general  operand, either register or implied memory.  For
     registers, it will be expressed as %r for one of the 8-bit registers,
     and for memory it will be expressed as M in  the  instruction  syntax
                                                                           8080

                      CROSS-Microcomputer cross assembler                    18


     and MEM[.(%H|%L)] in the description of the instruction.

   - %rp  - a register pair from the set {%B|%C, %D|%E, %H|%L %SP}.  These
     would be written, in the assembler, as %B, %D, %H or %SP.

   - %rpn - a register pair from the set {%PSW, %A, %B|%C, %D|%E, %H%L}.

   - Written as %PSW, %SP, %B, %D or %H.

II.3. Syntax
   - %A,%B,%C,%D,%E,%H,%L - 8-bit registers

   - %PSW,%SP,%B,%D,%H - where appropriate, 16-bit registers

   - M - memory, addressed via %H|%L

   - Immediate data is represented by the expression which generates it

II.4. Opcodes
  The opcodes that are recognized for the 8080 are shown below.   The  function
is given in a BLISS-like notation (the dot operator means "contents of").

ACI i           %A = .%A + i + .c; {c,z,s,p}
ADC opnd        %A = .%A + opnd + .c
ADD opnd        %A = .%A + .opnd; {c,z,s,p}
ADI i           %A = .%A + i; {c,z,s,p}
ANA opnd        %A = .%A and .opnd; c = 0; {z,s,p}
ANI i           %A = .%A + i; c = 0; {z,s,p}
CALL m          MEM[.%SP-1], MEM[.%SP-1] = .pc; %SP = .%SP - 2; pc = m;
CC m            if .c then CALL m
CM m            if .s then CALL m
CMA             %A = not .%A; {note: c,z,s,p not changed}
CMC             c = not .c
CMP opnd        .%A - .opnd; {c,z,s,p}
CNC m           if not .c then CALL m
CNZ m           if not .z then CALL m
CP m            if not .s then CALL m
CPE m           if .p then CALL m
CPI i           .%A - i; {c,z,s,p}
CPO m           if not .p then CALL m
CZ m            if .z then CALL m
DAA             %A = DecimalAdjust(.%A); {c,z,s,p}
DAD %B          %H|%L = .(%H|%L) + .(%B|%C); {c}
DAD %D          %H|%L = .(%H|%L) + .(%D|%E); {c}
DAD %SP         %H|%L = .(%H|%L) + .%SP; {c}
DCR opnd        opnd = .opnd - 1; {z,s,p}
DCX %rp         %rp = .(%rp) - 1
DI              ie = 0
EI              ie= 1;
HLT
IN i            %A = .DEV[i];
INR opnd        opnd = .opnd + 1; {z,s,p}
                                                                           8080

                      CROSS-Microcomputer cross assembler                    19


INX %rp         %rp = .(%rp) + 1;
JC m            if .c then pc = m;
JM m            if .s then pc = m;
JMP m           pc = m;
JNC m           if not .c then pc = m;
JNZ m           if not .z then pc = m;
JP m            if not .s then pc = m;
JPE m           if .p then pc = m;
JPO m           if not .p then pc = m;
JZ m            if .z then pc = m;
LDA m           %A = .MEM[m];
LDAX %B         %A = .MEM[.(%B|%C)];
LDAX %D         %A = .MEM[.(%D|%E)];
LHLD m          %H = .MEM[m]; %L = .MEM[m+1];
LXI %rp,m       %rp = m;
MOV %r1,%r2     %r1 = .%r2;
MOV m,%r        MEM[m] = .%r;
MOV %r,m        %r = .MEM[m];
MVI opnd,i      opnd = i;
NOP             ;
ORA opnd        %A = .%A or .opnd; c = 0; {z,s,p}
ORI i           {%A = .%A or i;}; c = 0; {z,s,p}
OUT i           DEV[i] = .%A;
PCHL            pc = .(%H|%L);
POP %rpn        %rpn = .MEM[.%SP], .MEM[.%SP + 1]; %SP = .%SP + 2;
PUSH %rpn       %SP = .%SP - 2; MEM[.%SP], MEM[.%SP + 1] = .%rpn;
RAL             c|%A = .(c|%A) lsh 1;
RAR             c|%A = .(c|%A) lsh -1;
RC              if .c then RET;
RET             pc = .MEM[.%SP], .MEM[.%SP+1]); %SP=.%SP + 2;
RLC             c = .%A<7,1>; %A = .%A lsh 1
RM              if .s then RET;
RNC             if not .c then RET;
RNZ             if not .z then RET;
RP              if not .s then RET;
RPE             if .p then RET;
RPO             if not .p then RET;
RRC             c = .%A<0,1>; %A = .%A lsh -1;
RST v           CALL v lsh 8;
RZ              if .z then RET;
SBB opnd        %A = .%A - .opnd - .c; {c,z,s,p}
SBI i           %A = .%A - i - .c; {c,z,s,p}
SHLD m          MEM[m] = .%H; MEM[m+1] = .%L;
SPHL            %sp = .(%H|%L);
STA m           MEM[m] = .%A;
STAX %B         MEM[.(%B|%C)] = .%A;
STAX %D         MEM[.(%D|%E)] = .%A;
STC             c = 1;
SUB opnd        %A = .%A - .opnd; {c,z,s,p}
SUI i           %A = .%A - i; {c,z,s,p}
XCHG            %D <=> %H; %E <=> %L;
XRA opnd        %A = .%A xor .opnd; c = 0; {z,s,p}
                                                                           8080

                      CROSS-Microcomputer cross assembler                    20


XTHL            MEM[.%SP - 1] <=> %H; MEM[.%SP] <=> %L;



















































                                                                           8080

                      CROSS-Microcomputer cross assembler                    21


III. Z80 syntax

III.1. Introduction
  The  Z80  portion of CROSS is not intended to correspond to the Zilog syntax;
instead, it is treated as an extension of  the  8080  operations  described  in
section  II.    This means that new opcode designators have been invented where
appropriate.

III.2. Machine State
  The Z80 registers are designated exactly like the 8080  registers,  with  the
following additions:

   - %X - index register X (16 bits)

   - %Y - index register Y (16 bits)

   - iv - the interrupt vector base address (8 bits)

   - ra - the dynamic RAM refresh address (8 bits)

III.3. Notation
  The following notational extensions are made to the 8080 description:

   - b - A bit position, 0-7, for bit operations

   - opnd  -  In  addition to %r and M, indexed operands are permitted for
     all instructions which use opnd; these are expressed to the assembler
     as d(X)  or  d(Y),  where  d  is  an  8-bit  displacement.    In  the
     description, they are interpreted as ".%X+d" or ".%Y+d".

   - %rpx - Register pair including %X, i.e., {%B|%C, %D|%E, %X, %SP}

   - %rpy - Register pair including %Y, i.e., {%B|%C, %D|%E, %Y, %SP}

III.4. Opcodes
  The extended opcodes for the Z80 are given below.  Those which are underlined
are  mnemonics  which  are neither 8080 instructions nor those defined by Zilog
for the Z80; they have been invented for CROSS.    A  complete  transliteration
from Zilog assembler format to CROSS syntax is given in section III.5.

BIT b,opnd      z = not .opnd<b,1>
CCD             .%A - .MEM[.(%H|%L)]; (%H|%L) = .(%H|%L) - 1;
                (%B|%C) = .(%B|%C) - 1; {z,s,p}
CCDR            until .%A eql .MEM[.(%H|%L)] or .(%B|%C) eql 0 do begin
                .%A - .MEM[.(%H|%L)]; (%H|%L) = .(%H|%L) - 1;
                (%B|%C) = .(%B|%C) - 1 end; {c,z,p}
CCI             .%A - .MEM[.(%H|%L)]; (%H|%L) = .(%H|%L) + 1;
                (%B|%C) = .(%B|%C) - 1; {z,s,p}
CCIR            until .%A eql .MEM[.(%H|%L)] or .(%B|%C) eql 0 do begin
                .%A - .MEM[.(%H|%L)]; (%H|%L) = .(%H|%L) + 1;
                (%B|%C) = .(%B|%C) - 1 end; {c,z,p}
CNO             CPO;
                                                                            Z80

                      CROSS-Microcomputer cross assembler                    22


CO              CPE;
DADC %rp        (%H|%L) = .(%H|%L) + .%rp + .c; {c,z,n,p}
DADX %rpy       %X = .%X + .%rpy; {c,n}
DADY %rpx       %Y = .%Y + .%rpx; {c,n}
DJNZ i          if .%B @z() 0 then pc = .pc + 2 + i
DSBC %rp        (%H|%L) = .(%H|%L) - .%rp - .c; n = 1; p = 0; {c,z}
EXAF            (%A|%PSW) <=> (%A'|%PSW');
EXX             (%B|%C) <=> (%B'|%C'); (%D|%E) <=> (%D'|%E'); (%H|%L) <=>
                (%H'|%L')
IM0
                im = 0;
IM1
                im = 1;
IM2             im = 2;
IND
INDR
INI
INIR
INP
JMPR i          pc = .pc + 2 + i;
JNO m           JPO m;
JO m            JPE m;
JRC i           if .c then JR i;
JRNC i          if not .c then JR i;
JRNZ i          if not .z then JR i;
JRZ i           if .z then JR i;
LBCD m          (%B|%C) = .MEM[m];
LDAI            %A = .iv;
LDAR            %A = .ra;
LDD             MEM[.(%D|%E)] = .MEM[.(%H|%L)]; (%D|%E) = .(%D|%E) - 1;
                (%H|%L) = .(%H|%L) - 1; (%B|%C) = .(%B|%C) - 1; n = 0;
LDDR            until .(%B|%C) eql 0 do begin MEM[.(%D|%E)] = .MEM[.(%H|%L)];
                (%D|%E) = .(%D|%E) - 1; (%H|%L) = .(%H|%L) - 1;
                (%B|%C) = .(%B|%C) - 1; end;
LDED m          (%D|%E) = .MEM[m];
LDI             .MEM[.(%D|%E)] = .MEM[.(%H|%L)]; (%D|%E) = .(%D|%E) + 1;
                (%H|%L) = .(%H|%L) + 1; (%B|%C) = .(%B|%C) - 1; {p}
LDIR            until .(%B|%C) eql 0 do begin MEM[.(%D|%E)] = .MEM[.(%H|%L)];
                (%D|%E) = .(%D|%E) + 1; (%H|%L) = .(%H|%L) + 1;
                (%B|%C) = .(%B|%C) - 1; end;
LIXD m          %X = .MEM[m+1], .MEM[m];
LIYD m          %Y = .MEM[m+1], .MEM[m];
LSPD m          %SP = .MEM[m+1], .MEM[m];
NEG             %A = - .%A; p = 0; {c,z,s}
OUTD
OUTDR
OUTI
OUTIR
OUTP
PCIX            pc = .%X;
PCIY            pc = .%Y;
RALR
                                                                            Z80

                      CROSS-Microcomputer cross assembler                    23


RARR
RES b,opnd      %opnd<b,1> = 0;
RETI            return from interrupt
RETN            return from nonmaskable interrupt
RLCR
RLD             decimal arithmetic
RNO             RPO;
RO              RPE;
RRCR
RRD             decimal arithmetic
SBCD m          MEM[m] = .(%B|%C);
SDED m          MEM[m] = .(%D|%E);
SET b,opnd      opnd<b,1> = 1;
SIXD m          MEM[m] = .%X;
SIYD m          MEM[m] = .%Y;
SLAR
SPIX            %SP = .%X;
SPIY            %SP = .%Y;
SRAR
SRLR
SSPD m          MEM[m] = .%SP;
STAI            iv = .%A;
STAR            ra = .%A;
XTIX            %X <=> MEM[.%SP];
XTIY            %Y <=> MEM[.%SP];

III.5. Z80 Transliterations
  The  following  transliterations  are  necessary  because  of the differences
between the Zilog definition of the instructions and the CROSS syntax.  This is
indexed  alphabetically  by  the  Zilog  operations  in  order  to   facilitate
translation of Zilog assembly programs to CROSS.

Zilog           CROSS ADC i    ACI i
ADC (HL)        ADC M
ADC HL,rp       DADC %rp
ADC (IX+d)      ADC d(X)
ADC (IY+d)      ADC d(Y)
ADC r           ADC %r
ADD i           ADI i
ADD (HL)        ADD M
ADD HL,rp       DAD %rp
ADD (IX+d)      ADD d(X)
ADD (IY+d)      ADD d(Y)
ADD r           ADD %r
AND i           ANI i
AND (HL)        ANA M
AND (IX+d)      ANA d(X)
AND (IY+d)      ANA d(Y)
AND r           ANA %r
BIT b,(HL)      BIT b,M
BIT b,(IX+d)    BIT b,d(X)
BIT b,(IY+d)    BIT b,d(Y)
                                                           Z80 transliterations

                      CROSS-Microcomputer cross assembler                    24


CALL m          CALL m
CALL C,m        CC m
CALL M,m        CM m
CALL NC,m       CNC m
CALL NZ,m       CNZ m
CALL NZ,m       CNZ m
CALL P,m        CP m
CALL PE,m       CPE m
CALL PO,m       CPO m
CALL Z,m        CZ m
CCF             CMC
CP i            CPI i
CP (HL)         CMP M
CP (IX+d)       CMP d(X)
CP (IY+d)       CMP d(Y)
CP r            CMP %r
CPD             CCD
CPDR            CCDR
CPI             CCI
CPIR            CCIR
CPL             CMA
DAA             DAA
DEC (HL)        DCR M
DEC IX          DCX %X
DEC IY          DCX %Y
DEC (IX+d)      DCR d(X)
DEC (IY+d)      DCR d(Y)
DEC rp          DCX %rp
DEC r           DCR %r
DI              DI
DJNZ d          DJNZ d
EI              EI
EX AF,AF'       EXAF
EX DE,HL        XCHG
EX (SP),HL      XTHL
EX (SP),IX      XTIX
EX (SP),IY      XTIY
EXX             EXX
HALT            HLT
IM 0            IM0
IM 1            IM1
IM 2            IM2
IN A,i          IN i
IN r,(c)
INC (HL)        INR M
INC IX          INX %X
INC IY          INX %Y
INC (IX+d)      INR d(X)
INC (IY+d)      INR d(Y)
INC rp          INX %rp
IND             IND
INDR            INDR
                                                           Z80 transliterations

                      CROSS-Microcomputer cross assembler                    25


INI             INI
INIR            INIR
JP m            JMP m
JP M,m          JM m
JP NC,m         JNC m
JP NZ,m         JNZ m
JP NZ,m         JNZ m
JP P,m          JP m
JP PE,m         JPE m
JP PO,m         JPO m
JP Z,m          JZ m
JR d            JMPR d
JR M,m          JRM m
JR NC,m         JRNC m
JR NZ,m         JRNZ m
JR NZ,m         JRNZ m
JR P,m          JRP m
JR PE,m         JRPE m
JR PO,m         JRPO m
JR Z,m          JRZ m
LD A,(m)        LDA m
LD A,(BC)       LDAX %B
LD A,(DE)       LDAX %D
LD A,i          MVI %A,i
LD A,r          MOV %A,%r
LD (m),A        STA m
LD (m),BC       SBCD m
LD (m),DE       SDED m
LD (m),HL       SHLD m
LD (m),IX       SIXD m
LD (m),IY       SIYD m
LD (m),SP       SSPD m
LD (BC),A       STAX %B
LD (DE),A       STAX %D
LD HL,(m)       LHLD m
LD (HL),i       MVI i
LD (HL),r       MOV %r,M
LD I,A          STAI
LD IX,(m)       LIXD m
LD IX,m         LXI %X,m
LD (IX+d),i     MVI i,d(X)
LD (IX+d),r     MOV %r,d(X)
LD IY,(m)       LIYD m
LD IY,m         LXI %Y,m
LD (IY+d),i     MVI i,d(Y)
LD (IY+d),r     MOV %r,d(Y)
LD r,A          MOV %r,%A
LD r,i          MVI %r,i
LD r,(HL)       MOV %r,M
LD r,(IX+d)     MOV %r,d(X)
LD r,(IY+d)     MOV %r,d(Y)
LD r,r          MOV %r,%r
                                                           Z80 transliterations

                      CROSS-Microcomputer cross assembler                    26


LD BC,(m)       LBCD m
LD DE,(m)       LDED m
LD HL,(m)       LHLD m
LD SP,(m)       LSPD m
LD IX,(m)       LIXD m
LD IY,(m)       LIYD m
LD rp,m         LXI %rp,m
LD SP,HL        SPHL
LD SP,IX        SPIX
LD SP,IY        SPIY
LDD             LDD
LDDR            LDDR
LDI             LDI
LDIR            LDIR
NEG             NEG
NOP             NOP
OR i            ORI i
OR (HL)         ORA M
OR (IX+d)       ORA d(X)
OR (IY+d)       ORA d(Y)
OR r            ORA %r
OUT (i),r
OUT i,A         OUT i
OUTD            OUTD
OUTDR           OUTDR
OUTI            OUTI
OUTIR           OUTIR
POP IX          POP %X
POP IY          POP %Y
POP rp          POP %rp
PUSH IX         PUSH %X
PUSH IY         PUSH %Y
PUSH rp         PUSH %rp
RES b,(HL)      RES b,M
RES b,(IX+d)    RES b,d(X)
RES b,(IY+d)    RES b,d(Y)
RES b,r         RES b,%r
RET             RET
RET M           RM
RET NC          RNC
RET NZ          RNZ
RET NZ          RNZ
RET P           RP
RET PE          RPE
RET PO          RPO
RET Z           RZ
RETI            RETI
RETN            RETN
RL (HL)         RALR M
RL (IX+d)       RALR d(X)
RL (IY+d)       RALR d(Y)
RL r            RALR %r
                                                           Z80 transliterations

                      CROSS-Microcomputer cross assembler                    27


RLA             RAL
RLC (HL)        RLC M
RLC (IX+d)      RLC d(X)
RLC (IY+d)      RLC i<d>(Y)
RLC r           RLC %r
RLCA            RLC
RLD             RLD
RR (HL)         RARR M
RR (IX+d)       RARR d(X)
RR (IY+d)       RARR d(Y)
RR r            RARR %r
RRA             RAR
RRC (HL)        RRC M
RRC (IX+d)      RRC d(X)
RRC (IY+d)      RRC d(Y)
RRC r           RRC %r
RRCA            RRC
RRD             RRD
RST v           RST v
SBC i           SBI i
SBC (HL)        SBC M
SBC HL,rp       DSBC %rp
SBC (IX+d)      SBC d(X)
SBC (IY+d)      SBC d(Y)
SBC r           SBC %r
SCF             STC
SET b,(HL)      SET b,M
SET b,(IX+d)    SET b,d(X)
SET b,(IY+d)    SET b,d(Y)
SET b,r         SET b,%r
SLA (HL)        SLAR M
SLA (IX+d)      SLAR d(X)
SLA (IY+d)      SLAR d(Y)
SLA r           SLAR %r
SRA (HL)        SRAR M
SRA (IX+d)      SRAR d(X)
SRA (IY+d)      SRAR d(Y)
SRA r           SRAR %r
SRL (HL)        CB3E
SRL (IX+d)      DDCBdd3E
SRL (IY+d)      FDCBdd3E
SRL r           CB??
SUB i           SUI i
SUB (HL)        SUB M
SUB (IX+d)      SUB d(X)
SUB (IY+d)      SUB d(Y)
SUB r           SUB %r
XOR i           XRI i
XOR (HL)        XRA M
XOR (IX+d)      XRA d(X)
XOR (IY+d)      XRA d(Y)
XOR r           XRA %r
                                                           Z80 transliterations

                      CROSS-Microcomputer cross assembler                    28


IV. 8008
  The 8008 is described by two different sets of opcodes.  The one set is based
upon  the  8080  style of coding, and is a subset of the operations.  The other
set is based upon the original set of 8008 mnemonics  as  described  by  Intel.
Rather  than  give  complete  descriptions  of  these  operations,  the user is
referred back to the 8080 descriptions.  What  this  section  will  give  is  a
listing  of the available operations and a cross reference to the original 8008
mnemonics.

  Note that the 8008 is "software compatible" with the 8080; the same mnemonics
will produce different bit patterns for the 8008 and the 8080.

IV.1. 8080 subset
  The instructions which are implemented for the 8008 are:

    ACI     ADC     ADD     ADI     ANA     ANI     CALL    CC      CM
    CMP     CNC     CNZ     CP      CPE     CPI     CPO     CZ      DCR
    HLT     IN      INR     JC      JM      JMP     JNC     JNZ     JP
    JPE     JPO     JZ      MOV     MVI     NOP     ORA     ORI     OUT
    RAL     RAR     RC      RET     RLC     RM      RNC     RNZ     RP
    RPE     RPO     RRC     RST     RZ      SBB     SBI     SUB     SUI
    XRA     XRI

  The set of original 8008 operations are defined as:

8080            Original 8008
ADC             ACA, ACB, ACC, ACD, ACE, ACH, ACL
ACI             ACI
ADD             ADA, ADB, ADC, ADD, ADE, ADH, ADL
ADI             ADI
CALL            CAL
CNC             CFC
CPO             CFP
CM              CFS
CNZ             CFZ
CMP             CPA, CPB, CPC, CPD, CPE, CPH, CPL
CPI             CPI
CC              CTC
CPE             CTP
CP              CTS
CZ              CTZ
DCR             DCB, DCC, DCD, DCE, DCH, DCL
HLT             HLT
INR             INB, INC, IND, INE, INH, INL
IN              INP
JNC             JFC
JNZ             JFZ
JPO             JFP
JM              JFS
JMP             JMP
JC              JTC
JPE             JTP
                                                                           8008

                      CROSS-Microcomputer cross assembler                    29


JP              JTS
JZ              JTZ
MOV             LAA, LAB, LAC, LAD, LAE, LAH, LAL, LAM, 
                LBA, LBB, LBC, LBD, LBE, LBH, LBL, LBM, 
                LCA, LCB, LCC, LCD, LCE, LCH, LCL, LCM, 
                LDA, LDB, LDC, LDD, LDE, LDH, LDL, LDM, 
                LEA, LEB, LEC, LED, LEE, LEH, LEL, LEM, 
                LHA, LHB, LHC, LHD, LHE, LHH, LHL, LHM, 
                LLA, LLB, LLC, LLD, LLE, LLH, LLL, LLM
MVI             LAI, LBI, LCI, LDI, LEI, LHI, LLI, LMI
ANA             NDA, NDB, NDC, NDD, NDE, NDH, NDL, NDM
ANI             NDI
NOP             NOP
ORA             ORA, ORB, ORC, ORD, ORE, ORH, ORL, ORM
ORI             ORI
OUT             OUT
RAL,RAR         RAL, RAR
RET             RET
RNC             RFC
RPO             RFP
RP              RFS
RNZ             RFZ
RLC,RRC         RLC, RRC
SUB             SBA, SBB, SBC, SBD, SBE, SBH, SBL, SBM
SBI             SBI
SBC             SUA, SUB, SUC, SUD, SUE, SUH, SUL, SUM
SUI             SUI
XRA             XRA, XRB, XRC, XRD, XRE, XRH, XRL, XRM
























                                                                           8008

                      CROSS-Microcomputer cross assembler                    30


V. 8048

V.1. Machine State

   - R0-R7 general registers R0 thru R7; R0 and R1 can be used as indirect
     memory reference registers.

   - Bus<0,8> Bus register port (latched output, unlatched input)

   - MB - Temporary location which holds result of last SEL mb.

   - MEM - Addressible memory

   - P1<0,8>-P7<0,8> I/O or expansion ports P1 thru P7

   - PSW<0,8>  Program  status  word.    The following bits in the PSW are
     named:

        * SP = PSW<0,3> Stack pointer

        * RB = PSW<4,1> Register bank select

        * f1 = PSW<4,1> Software flag F1 (same as RB)

        * f0 = PSW<5,1> Software flag F0

        * ac = PSW<6,1> Auxiliary Carry status bit

        * c = PSW<7,1> Carry status bit

     A<0,8> Accumulator

   - S[0:7]<0,16> Stack

   - T0 Timer/counter timeout flag; external pin T0

   - T1 Counter decrement request; external pin T1

V.2. Notation
  The operands are:

   - A - accumulator

   - acf0f1 - A, c, F0, F1

   - addr - 12-bit address specifying a memory byte

   - ai - analog input 0 or 1

   - BUS - bus input-output register

   - c - carry bit
                                                                           8048

                      CROSS-Microcomputer cross assembler                    31


   - data - 8-bit immediate data

   - dev - an I/O device

   - ep - expander port P4, P5, P6 or P7

   - F0,F1 - status bits

   - f - status bits F0 or F1

   - I - interrupt signal

   - TCNTI - timer or interrupt signal

   - int - I or TCNTI

   - MB0,MB1 - memory bank select

   - mb - MB0, MB1

   - P1-P7 - I/O or expansion ports

   - port - I/O port P1 or P2

   - R0-R7 - registers R0-R7

   - r - register R0 or R1

   - @r - memory location MEM[.r]

   - rn - register R0-R7

   - RB0,RB1 - Register bank select

   - rb - RB0, RB1

   - reg - A, R0-R7

   - src-opnd - MEM[.r], data or .rn

V.3. Syntax
  Immediate data is expressed as # followed by the data.

V.4. Opcodes

ADD A,src-opnd  A = .A + src-opnd;
ADDC A,src-opnd A = .A + src-opnd + .c;
ANL port,data   port = .port and data;
ANL A,src-opnd  A = .A and src-opnd;
ANL BUS,data    Bus = .Bus and data;
ANLD ep,A       ep = ep and .A<0,4>;
CALL addr       SP = .SP + 1; Stack[.SP]<0,16> = (.PC<0,8>|.PSW<4,4>|.PC<8,4>);
                                                                           8048

                      CROSS-Microcomputer cross assembler                    32


                PC<11,1> = .MB; PC<0,11> = addr;
CLR acf0f1      acf0f1 = 0;
CPL acf0f1      acf0f1 = not .acf0f1;
DA A
DEC reg         reg = .reg - 1;
DIS int
DJNZ rn,addr8
EN int
ENT0 CLK        Enable timer output on pin T0
IN A,port       A = port;
INC A,@r        MEM[.r] = .MEM[.r] + 1;
INS A,BUS       A = .Bus;
JBn addr8       if .A<n,1> then PC<0,8> = addr8;
JC addr8        if .c then PC<0,8> = addr8;
JFf addr8       if .f then PC<0,8> = addr8;
JMP addr        PC<11,1> = .MB; PC<0,11> = addr;
JMPP @A         PC<0,8> = .(.PC<8,4>|.A);
JNC addr8       if not .c then PC<0,8> = addr8;
JNI addr8       if not .i then PC<0,8> = addr8;
JNTn addr8      if not .tn then PC<0,8> = addr8;
JNZ addr8       if not .z then PC<0,8> = addr8;
JTF addr8
JTn             if .tn then PC<0,8> = addr8;
JZ addr8        if .z then PC<0,8> = addr8;
MOV A,@r        A = .MEM[.r];
MOV A,T         A = .T;
MOV @r,A         MEM[.r] = .A;
MOV @r,data     MEM[.reg] = data;
MOV reg,data    reg = data;
MOV A,rn        A = .rn;
MOV PSW,A       PSW = .A;
MOV T,A         T = .A;
MOV rn,A        rn = .A;
MOVD A,ep       A<0,4> = ep;
MOVD ep,A       ep = .A<0,4>;
MOVP A,@A       A = .MEM[(.PC<8,4>|.A)];
MOVP3 A,@A      A = .MEM[(3|.A)];
MOVX @r,A       MEM[.r] = .A;
MOVX A,@r       A = .MEM[.r];
NOP             ;
ORL port,data   port = .port or data;
ORL A,src-opnd  A = .A + src-opnd;
ORL BUS,data    Bus = .Bus or data;
ORLD ep,A       ep = .ep or .A;
OUTL port,A     port = .A;
OUTL BUS,A      Bus = .A;
RAD A           A = D;
RET             PC<0,12> = (.Stack[.SP]<0,4>|.Stack[.SP]<8,8>); SP = .SP - 1;
RETR            PC<0,12> = (.Stack[.SP]<0,4>|.Stack[.SP]<8,8>);
                PSW<4,4> = .Stack[.SP]<4,4>; SP = .SP -1;
RL A            A = .A rot 1;
RLC A           (c|A) = .(c|A) rot 1;
                                                                           8048

                      CROSS-Microcomputer cross assembler                    33


RR A            A = .A rot -1;
RRC A           (c|A) = .(c|A) rot -1;
SEL ai          select analog input ai
SEL mb          MB = mb;
SEL rb
STOP TCNT       Stop counter or timer mode
STRT CNT        Counter increments on falling edge of T1
STRT T          Counter increments every 480 system clock ticks
SWAP A          .A<0,4> <=> .A<4,4>;
XCH A,@r        A <=> MEM[.r];
XCH A,rn        A <=> rn;
XCHD A,@r       A<0,4> <=> MEM[.r]<0,4>;
XRL A,src-opnd  A = .A xor opnd;







































                                                                           8048

                      CROSS-Microcomputer cross assembler                    34


VI. 1802

VI.1. Machine State

D               The data register

DF              The "data flag" register, or carry

P               4-bit program counter pointer

X               4-bit data counter pointer

T               8-bit buffer for P and X

Q               Q-status output register

VI.2. Opcodes
  The operation codes recognized for the 1802 are:

ADC             D = .mem[.R[.X]] + .D + .DF
ADCI            D = data8 + .D + .DF
ADD             D = .mem[.R[.X]] + .D
ADI             D = data8 + .D
AND
ANI
BDF             if .DF then R[P]<7,0> = adr8
BGE
BL
BM
BNF
BNQ
BNZ
BN1
BN2
BN3
BN4
BPZ
BQ
BR
BZ
B1
B2
B3
B4
DEC n           R[n] = .R[n] - 1;
DIS
GHI
GLO
IDL
INC n           R[n = .R[n] + 1;
INP
IRX
                                                                           1802

                      CROSS-Microcomputer cross assembler                    35


LBDF
LBNF
LBNQ
LBNZ
LBQ
LBR
LBZ
LDA
LDI
LDN
LDX
LDXA
LSDF
LSIE
LSKP
LSNF
LSNQ
LSNZ
LSQ
LSZ
MARK
NBR
NLBR
NOP
OR
ORI
OUT
PHI
PLO
REQ
RET
RSHL
RSHR
SAV
SD
SDB
SDBI
SDI
SEP
SEQ
SEX
SHL
SHLC
SHR
SHRC
SKP
SM
SMB
SMBI
SMI
STR
STXD
                                                                           1802

                      CROSS-Microcomputer cross assembler                    36


XOR
XRI


















































                                                                           1802

                      CROSS-Microcomputer cross assembler                    37


VII. 6502

VII.1. Machine state
  The machine state is represented by:

   - c - The carry bit

   - z - The zero bit, true if result was zero

   - v - The overflow bit

   - s - The sign bit, true if result was negative

   - d - Decimal mode

   - i - Interrupt disable bit; 0 => interrupts enabled

   - b - Breakpoint flag; set by BRK instruction trap

  The machine registers are:

   - ac<0,8> - The single accumulator

   - x<0,8> - index register x, preindexes indirect addresses

   - y<0,8> - index register y, postindexes indirect addresses.

   - sp<0,8> - stack pointer.

   - psw<0,8> - processor status word.

VII.2. Notation
  The operands are expressed as:

   - opnd8 - 8 bit operand corresponding to one of the form:

        * addr - Base page direct (8 bit address).

        * addr,X - Base page indexed by x; MEM[addr + .x].

        * (addr,X) - Indexed indirect by x; (.MEM[addr + .x]).

        * (addr),Y - Indexed indirect by y; (.MEM[addr] + .y).

   - opnd16 - Any of the following operands in the form:

        * addr - Extended direct (16 bit address); MEM[addr].

        * addr,X - Absolute indexed via x; MEM[addr + .x].

        * addr,Y - Absolute indexed via y; MEM[addr + .y].

                                                                           6502

                      CROSS-Microcomputer cross assembler                    38


   - opnd - Either opnd8 or opnd16.

   - i - Immediate data, expressed as #expression.

VII.3. Syntax
  The syntax for operands is much like that specified by MOS Technology.

  Immediate  operands  are indicated by preceding the operand with a hash mark,
#. 

  X- or Y- indexed operands are written as a suffix ",X" or ",Y".

VII.4. Opcodes
  The opcodes recognized for the Mos Technology 6502 are:

ADC opnd        ac = .ac + .opnd + .c; {s,z,c,v}
ADC i           ac = .ac + i + .c; {s,z,c,v}
AND opnd        ac = .ac and .opnd; {s,z}
AND i           ac = .ac and i; {s,z}
ASL opnd        c|opnd = opnd lsh 1; {s,z,c}
BCC d           if not .c then pc = .pc + 1 + d;
BCS d           if .c then pc = .pc + 1 + d;
BEQ d           if .z then pc = .pc + 1 + d;
BGE d           if .c then pc = .pc + 1 + d; Synonym for BCS
BIT opnd        .ac and .opnd; s = (.ac and .opnd)<7,1>;
                v = (.ac and .opnd)<6,1>; {z}
BLT d           if not .c then pc = .pc + 1 + d; Synonym for BCC
BMI d           if .s then pc = .pc + 1 + d;;
BNE d           if not .z then pc = .pc + 1 + d;;
BPL d           if not .s then pc = .pc + 1 + d;;
BRK             MEM[.sp] = .pc<0,8>; MEM[.sp + 1] = .pc<8,8>;
                MEM[.sp + 2] = .psw; sp = .sp - 3; pc = $FFFFFFFE; i = 1;
                b = 1;
BVC d           if not .v then pc = .pc + 1 + d;;
BVS d           if .v then pc = .pc + 1 + d;;
CLC             c = 0;
CLD             d = 0;
CLI             i = 0;
CLV             v = 0;
CMP opnd        .ac - .opnd; {s,z,c}
CPX opnd        .x - .opnd; {s,z,c}
CPY opnd        .y - opnd; {s,z,c}
DEC             ac = .ac - 1; {s,z}
DEX             x = .x - 1; {s,z}
DEY             y = .y - 1; {s,z}
EOR opnd        ac = .ac - .opnd
INC             ac = .ac + 1; {z,s}
INX             x = .x + 1;
INY             y = .y + 1;
JMP m           pc = m;
JSR m           MEM[.sp] = .pc<8,8>; MEM[.sp - 1] = .pc<0,8>; sp = .sp - 2;
                pc = m;
                                                                           6502

                      CROSS-Microcomputer cross assembler                    39


LDA opnd        ac = .opnd; {s,z}
LDX opnd        x = .opnd; {s,z}
LDY opnd        y = .opnd; {s,z}
LSR             ac|c = .ac|0 lsh -1;
NOP             ;
ORA opnd        ac = .ac or opnd; {s,z}
PHA             MEM[.sp] = .ac; sp = .sp - 1;
PHP             MEM[.sp] = .psw; sp = .sp - 1;
PLA             ac = .MEM[.sp + 1]; sp = .sp + 1;
PLP             psw = .MEM[.sp + 1]; sp = .sp + 1;
ROL opnd        c|.MEM[opnd] = c|.MEM[opnd] rot 1; {s,z,c}
ROR opnd        c|.MEM[opnd] = c|.MEM[opnd] rot -1; {s,z,c}
RTI             psw = .MEM[.sp + 1]; pc<0,8> = .MEM[.sp + 2];
                pc<8,8> = .MEM[.sp + 3]; sp = .sp + 3; pc = .pc + 1;
RTS             pc<0,8> = .MEM[.sp + 1]; pc<8,8> = .MEM[.sp + 2]; sp = .sp + 2;
                pc = .pc + 1;
SBC opnd        ac = .ac - .opnd - (not .c); {s,z,c,v}
SEC             c = 1;
SED             d = 1;
SEI             i = 1;
STA opnd        MEM[opnd] = .ac; {s,z}
STX opnd        MEM[opnd] = .x; {s,z}
STY opnd        MEM[opnd] = .y; {s,z}
TAX             a = .x;
TAY             a = .y;
TSX             sp = .x;
TXA             x = .a;
TXS             x = .sp;
TYA             y = .a;























                                                                           6502

                      CROSS-Microcomputer cross assembler                    40


VIII. 6800

VIII.1. Machine State
  The registers are:

   - %A<0,8> - accumulator A

   - %B<0,8> - accumulator B

   - %X<0,16> - Index register

   - sp<0,16> - Stack pointer

   - pc<0,16> - The program counter

  The flags are:

   - c - Carry

   - o - Overflow

   - s - Sign

   - z - Zero

   - xc - Auxiliary carry

VIII.2. Notation

   - mem - A memory address which can be one of

        * Base page direct (.MEM[mem], mem 8 bits)

        * Extended direct (MEM[mem], mem 16 bits)

        * Indexed (MEM[mem+.%X], mem 8 bits)

   - memd - A memory address which can be one one of

        * Extended direct (MEM[memd], memd 16 bits)

        * Indexed (MEM[memd+.%X], memd 8 bits)

   - i - An immediate operand, written as #i

   - i16 - A 16-bit immediate operand, written as #i16

   - d - A displacement, usually written as an address; CROSS will compute
     the  actual  displacement  between  the  current  instruction and the
     destination address.

   - opnd - A general operand; may be either mem or i.   When  interpreted
                                                                           6800

                      CROSS-Microcomputer cross assembler                    41


     as  a  value,  ".opnd"  may  represent either .MEM[mem] or i.  Please
     excuse the somewhat sloppy notation; it makes  the  description  more
     compact.

   - sr - The status register which holds c,z,s,o,xc.

VIII.3. Syntax
  Immediate operands are written with a # symbol, e.g.

            ADDA #$F9       ; Adds hex F9 to A

  Indexing is specified by writing ",X" after the operand.  The operand must be
a value which will fit in 8 bits.

    foo==$10
            ADDA  foo,X

VIII.4. Opcodes

ABA             %A = .%A + .%B; {c,z,s,o,xc}
ADCA opnd       %A = .%A + .opnd + .c; {c,z,s,o,xc}
ADCB opnd       %B = .%B + .opnd + .c; {c,z,s,o,xc}
ADDA opnd       %A = .%A + .opnd; {c,z,s,o,xc}
ADDB opnd       %B = .%b + .opnd; {c,z,s,o,xc}
ANDA opnd       %A = .%A + .opnd; o=0; {z,s}
ANDB opnd       %B = .%B + .opnd; o=0; {z,s}
ASL memd        c=.memd<7,1>; memd=.memd lsh 1; o=.s xor .c; {z,s}
ASLA            c=.%A<7,1>; %A = .%A lsh 1; o=.s xor .c; {z,s}
ASLB            c=.%B<7,1>; %B = .%B lsh 1; o=.s xor .c; {z,s}
ASR memd        c=.memd<0,1>; memd=.memd ash -1; o=.s xor .c; {z,s}
ASRA            c=.%A<0,1>; %A=.%A ash -1; o=.s xor .c; {z,s}
ASRB            c=.%B<0,1>; %B=.%B ash -1; o=.s xor .c; {z,s}
BCC d           if not .c then BRA d;
BCS d           if .c then BRA d;
BEQ d           if .z then BRA d;
BGE d           if not (.o xor .s) then BRA d;
BGT d           if not (.z or (.s xor .o)) then BRA d;
BHI d           if not (.c or .z) then BRA d;
BHS d           if not .c then BRA d; Synonym for BCC
BITA mem        .%A and .mem; o = 0; {z,s}
BITB mem        .b and .mem; o = 0; {z,s}
BLE d           if .z or (.s xor .o) then BRA d;
BLO d           if .c then BRA d; Synonym for BCS
BLS d           if .c or .z then BRA d;
BLT             if .s xor .o then BRA d;
BMI d           if .s then BRA d;
BNE d           if not .z then BRA d;
BPL d           if not .s then BRA d;
BR d            BRA d;
BRA d           pc = .pc + 2 + d;
BSR d           MEM[.sp] = .pc<0,8>; MEM[.sp - 1] = .pc<8,8>; sp = .sp - 2;
                pc = .pc + d + 2;
                                                                           6800

                      CROSS-Microcomputer cross assembler                    42


BVC d           if not .o then BRA d;
BVS d           if .o then BRA d;
CBA             .%A - .%B; {c,z,s,o}
CLC             c=0;
CLI             ie = 0;
CLR memd        memd=0; c=0; z=1; s=0; o=0;
CLRA            %A = 0; c=0; z=1; s=0; o=0;
CLRB            %B = 0; c=0; z=1; s=0; o=0;
CLV             o = 0;
CMPA opnd       .%A - .opnd; {c,z,s,o}
CMPB opnd       .%B - .opnd; {c,z,s,o}
COM memd        memd=~.memd; c=1; o=0; {s,z}
COMA            %A=~.%A; c=1; o=0; {s,z}
COMB            %B=~.%B; c=1; o=0; {s,z}
CPX memd        %X<0,8>-.(memd+1); %X<8,8>-.memd; {s,z,o}
DAA             decimal arithmetic
DEC memd        memd=.memd-1; {s,z,o}
DECA            %A = .%A - 1; {s,z,o}
DECB            %B = .%B - 1; {s,z,o}
DES             sp = .sp - 1;
DEX             %X = .%X - 1; {z}
EORA opnd       %A=.%A xor .opnd; o=0; {s,z}
EORB opnd       %B=.%B xor .opnd; o=0; {s,z}
INC memd        memd=.memd+1; {s,z,o}
INCA            %A = .%A + 1; {s,z,o}
INCB            %B = .%B + 1; {s,z,o}
INS             sp = .sp + 1;
INX             %x = .%X + 1; {z}
JMP mem         pc = mem;
JSR mem         MEM[.sp]=.pc<0,8>; MEM[.sp-1]=.pc<8,8>; sp=.sp-2; pc=mem;
LDAAmem         A = .mem; o = 0; {o,s,z}
LDABmem         B = .mem; o = 0; {o,s,z}
LDS mem         sp<8,8>  = .mem; sp<0,8> = .(mem + 1); o = 0; {z,s}
LDS i16         sp = i16; {s,z}
LDX opnd        %X<8,8> = .opnd; %X<0,8> = .(opnd + 1); o = 0; {z,s}
LSRA            A = .A lsh -1;
LSRB            B = .B lsh -1;
NEG memd        memd = 0 -.memd; {c,s,z,o}
NEGA            %A = 0 - .%A; {c,s,z,o}
NEGB            %B = 0 - .%B; {c,s,z,o}
NOP             ;
ORAA opnd       %A=.%A or .opnd; o=0; {s,z}
ORAB opnd       %B=.%B or .opnd; o=0; {s,z}
PSHA            Synonym for PSHS A
PSHB            Synonym for PSHS B
PULA            Synonym for PULS A
PULB            Synonym for PULS B
ROL opnd        c|opnd = .(c|opnd) rot 1;
ROLA            c|A = .(c|A) rot 1;
ROLB            c|B = .(c|B) rot 1;
ROR opnd        c|opnd = .(c|opnd) rot -1;
RORA            c|A = .(c|A) rot -1;
                                                                           6800

                      CROSS-Microcomputer cross assembler                    43


RORB            c|B = .(c|B) rot -1;
RTI
RTS
SBA             %A = .%A - .%B; {c,z,s,o}
SBCA opnd       %A = %A - .opnd - .c; {c,z,s,o}
SBCB opnd       %B = .%B - .opnd - .c; {c,z,s,o}
SEC             c = 1;
SEI             ie = 1;
SEV             o = 1;
STAA opnd       mem = .%A;
STAB opnd       mem = .%B;
STS mem         mem = .sp<8,8>; (mem + 1) = .sp<0,8>; o=0; {s,z}
STX mem         mem = .%X<8,8>; (mem + 1) = .%X<0,8>; o=0; {s,z}
SUBA opnd       %A = .%A - .opnd; {c,s,z,o}
SUBB opnd       %B = .%B - .opnd; {c,s,z,o}
SWI             software interrupt;
TAB             %B = .%A; o=0; {s,z}
TAP             sr = .%A; {c,z,s,o,xc}
TBA             %A = .%B; o=0; {s,z}
TPA             %A = .sr
TST memd        c = 0; z = .memd eql 0; s = .memd < 0; o = 0;
TSTA            c = 0; z = .%A eql 0; s = .%A < 0; o = 0;
TSTB            c = 0; z = .%B eql 0; s = .%B < 0; o = 0;
TSX             %X = .sp + 1;
TXS             sp = .%X - 1;
WAI             MEM[.sp]=.pc<0,8>; MEM[.sp-1] = .pc<8,8>;
                MEM[.sp-2] = .%X<0,8>; MEM[.sp-3] = .%X<8,8>; MEM[.sp-4] = .%A;
                MEM[.sp-5] = .%B; MEM[.sp-6] = .sr; sp = .sp-7;
























                                                                           6800

                      CROSS-Microcomputer cross assembler                    44


IX. 6805
  There is one known bug in the 6805 code.  During pass 1, an indexedaddress is
assumed  to  require  2  bytes if it is a forward reference.  During pass 2, if
CROSS determines that the address can be  represented  in  one  byte,  it  will
assign  it  as one byte.  All labels and other position-dependent symbols after
this point will  now  have  different  values  assigned  during  pass  2;  thus
generating a phase (P) error.  This may be circumvented by explicitly using a >
operator to force the address to always be two bytes.

IX.1. Machine State

A<0,8>          Accumulator

X<0,8>          Index register

PC<0,11>        Program counter

CC<0,5>         Condition codes

                h               half-carry (CC<4,1>)

                i               interrupt mask (CC<3,1>)

                n               negative (sign) status (CC<2,1>)

                z               zero status (CC<1,1>)

                c               carry status (CC<0,1>)

                SP<0,11>
                Stack  pointer;  note  however  that  only SP<0,5> is variable;
                SP<5,6> is constant at ^B000011.

il              External interrupt line.

IX.2. Notation

data8           Any immediate 8-bit data.

opnd            Any operand in the modes direct, extended, indexed (no offset),
                indexed (8-bit offset), indexed (16-bit offset).

opnd8           Any operand in  the  modes  direct,  indexed  (no  offset),  or
                indexed (8-bit offset).

label           Any  operand which can be converted by CROSS to an 8-bit offset
                (7 bits plus sign).

IX.3. Syntax
  Immediate operands are preceded by #.

  A > symbol preceding an operand forces that operand to be two bytes.
                                                                           6805

                      CROSS-Microcomputer cross assembler                    45


  A < symbol preceding an operand forces that operand to be one byte.

  Indexing is indicated by following the operand with (X).

IX.4. Opcodes

ADC data8       A = .A + data8 + .c; {h,n,z,c}
ADC opnd        A = .A + .opnd + .c; {h,n,z,c}
ADD data8       A = .A + data8; {h,n,z,c}
ADD opnd        A = .A + .opnd; {h,n,z,c}
AND data8       A = .A and data8; {n,z}
AND opnd        A = .A and .opnd; {n,z}
ASL opnd8       opnd8 = .opnd8 ash 1; {n,z,c}
ASLA            A = .A ash 1; {n,z,c}
ASLX            X = .X ash 1; {n,z,c}
ASR opnd8       opnd8 = .opnd8 ash -1; {n,z,c}
ASRA            A = .A ash -1; {n,z,c}
ASRX            X = .X ash -1; {n,z,c}
BCC label       if not .c then BRA label;
BCLRn opnd8     opnd8<n,1> = 0;
BCS label       if .c then BRA label;
BEQ label
BHCC label      if not .h then BRA label;
BHCS label      if .h then BRA label;
BHI label
BHS label       if not .c then BRA label;
BIH label       if .il then BRA label;
BIL label       if not .il then BRA label;
BIT label       {n,z}
BLO label       if .c then BRA label;
BLS label
BMC label       if not .i then BRA label;
BMS label       if .i then BRA label;
BNE label       if not .z then BRA label;
BPL label       if not .n then BRA label;
BRA label       PC = .PC + signextended(label);
BRN label       ;
BRCLR opnd8,label
BRSET opnd8,label
BSETn opnd      opnd<n,1> = 1;
CLC             c = 0; {c}
CLI             i = 0; {i}
CLR opnd8       opnd8 = 0; n = 0; z = 1; {n,z}
CLRA            A = 0; n = 0; z = 1; {n,z}
CLRX            X = 0; n = 0; z = 1; {n,z}
CMP data        .A - data; {n,z,c}
CMP opnd        .A - .opnd; {n,z,c}
COM opnd8       opnd8 = not .opnd8; c = 1; {n,z,c}
COMA            A = not .A; c = 1; {n,z,c}
COMX            X = not .X; c = 1; {n,z,c}
CPX data        .X - data; {n,z,c}
CPX opnd        .X - .opnd; {n,z,c}
                                                                           6805

                      CROSS-Microcomputer cross assembler                    46


DEC opnd8       opnd8 = .opnd8 - 1 ; {n,z}
DECA            A = .A - 1; {n,z}
DECX            X = .X - 1; {n,z}
INC opnd8       opnd8 = .opnd8 + 1 ; {n,z}
INCA            A = .A + 1; {n,z}
INCX            X = .X + 1; {n,z}
JMP opnd
JSR opnd
LDA data        A = data; {n,z}
LDA opnd        A = .opnd; {n,z}
LDX data        X = data; {n,z}
LDX opnd        X = .opnd; {n,z}
LSL opnd8       opnd8 = .opnd8 lsh 1; {n,z,c}
LSLA            A = .A lsh 1; {n,z,c}
LSLX            X = .X lsh 1; {n,z,c}
LSR opnd8       opnd8 = .opnd8 lsh -1; n = 0; {n,z,c}
LSRA            A = .A lsh -1; n = 0; {n,z,c}
LSRX            X = .X lsh -1; n = 0; {n,z,c}
NEG opnd8       opnd8 = -.opnd8; {n,z,c}
NEGA            A = -.A; {n,z,c}
NEGX            X = -.X; {n,z,c}
NOP             ;
ORA data        A = .A or data; {n,z}
ORA opnd        A = .A or .opnd; {n,z}
ROL opnd8       (c|opnd8) = .(c|opnd8) rot 1; {n,z,c}
ROLA            (c|A) = .(c|A) rot 1; {n,z,c}
ROLX            (c|X) = .(c|X) rot 1; {n,z,c}
ROR opnd8       (c|opnd8) = .(c|opnd8) rot -1; {n,z,c}
RORA            (c|A) = .(c|A) rot -1; {n,z,c}
RORX            (c|X) = .(c|X) rot -1; {n,z,c}
RSP
RTI
RTS
SBC data        A = .A - data - .c; {n,z,c}
SBC opnd        A = .A - .opnd; {n,z,c}
SEC             c = 1; {c}
SEI             i = 1; {i}
STA opnd        opnd = .A; {n,z}
STOP
STX opnd        opnd = .X; {n,z}
SUB data        A = .A - data; {n,z,c}
SUB opnd        A = .A - .opnd; {n,z,c}
SWI
TAX             X = .A;
TST opnd8       .opnd8 - 0; {n,z}
TXA             A = .X;






                                                                           6805

                      CROSS-Microcomputer cross assembler                    47


X. 6809
  There is one known bug in the 6809 code.  During pass 1, a PC-relativeaddress
is  assumed to require 2 bytes if it is a forward reference.  During pass 2, if
CROSS determines that the address can be represented in one byte because it  is
less  than  256 locations ahead, it will assign it as one byte.  All labels and
other position-dependent symbols after  this  point  will  now  have  different
values  assigned during pass 2; thus generating a Phase (P) error.  This may be
circumvented by explicitly using a > operator to force the address to always be
two bytes.

X.1. Machine State

A<0,8>          Accumulator A

B<0,8>          Accumulator B

CC<0,8>         Condition codes

                e               "entire"  flag  -  indicates  action   on   RTI
                                instruction

                f               FIRQ interrupt request mask; 1 => disabled

                h               Aux carry (half carry); BCD arithmetic

                i               IRQ interrupt request mask; 1 => disabled

                s               Sign bit (1 => negative)

                z               Zero bit (1 => zero result)

                v               Overflow bit

                c               Carry bit

D<0,16>         A|B

DP<0,8>         Direct page register

PC<0,16>        program counter

S<0,16>         stack pointer register

U<0,16>         stack pointer register

X<0,16>         index register

Y<0,16>         index register




                                                                           6809

                      CROSS-Microcomputer cross assembler                    48


X.2. Notation

   - addr  -  any  of  the  permissible addressing modes, direct page, one
     byte, two byte, indexed, indirect, etc.

   - opnd8 - any one-byte operand, except immediate

   - opnd16 - any two-byte operand, except immediate

   - data8 - 8 bit immediate data

   - data16 - 16 bit immediate data

   - reglist - A list of register names from the set CC, A, B, DP, X, Y, U
     or S, PC

X.3. Syntax

   - A - accumulator A

   - B - accumulator B

   - CC - condition codes

   - D - accumulator D (=A|B)

   - DP - direct page register DP

   - PC - Program counter

   - PCR - Program counter relative addressing

   - S - Stack pointer S

   - U - Stack pointer U

   - X - Index register X

   - Y - Index register Y

  Binary values are indicated by preceding the value with a % symbol.

  Immediate operands are written with a # in front of the expression; the value
of the operand  or  an  explicit  size  specification,  either  with  <  or  >,
determines  if  it  is  a  data8  or  data16.  Those instructions which require
double-width immediate operands will force data16 values even if the value will
normally fit in a single byte.

  An explicit one-byte address or operand, opnd8, is designated by a < symbol.

  An explicit two-byte address or operand, opnd16, is designated by a > symbol.

                                                                           6809

                      CROSS-Microcomputer cross assembler                    49


  Indirect  operands  are  enclosed in [] symbols; an indirect operand can be a
one-byte or two-byte operand.  Indexed, autoincrement, and autodecrement  modes
are permitted.

  Indexing  is indicated by suffixing a ",r" to the operand, for various values
of index registers (X, Y, S, U, PC, PCR).

  Single auto-decrement of register operands is indicated by prefixing a single
- symbol; double auto-decrement by two such symbols: --.

  Single auto-increment of register operands is indicated by suffixing a single
+ symbol; double auto-increment by two such symbols: ++.

  Note that the form which omits the  comma  before  the  register  in  indexed
modes, which is used in the 6809 assembler, is not accepted by CROSS, e.g.,

    6809                    CROSS
    R+                      ,R+
    -R                      ,-R
    R                       ,R
    [R]                     [,R]
    <R                      <,R
    <[R]                    <[,R]
    >R                      >,R
    >[R]                    >[,R]

X.4. Opcodes

.SETDP addr     Indicates to the assembler that the direct page register refers
                to addr; any references to that page will be handled as direct
                page references.
ABX             X = .X + .B; Unsigned add
ADCA opnd       A = .A + .opnd + .c; {h,n,z,v,c}
ADCA data       A = .A + data + .c; {h,n,z,v,c}
ADCB opnd       B = .B + .opnd + .c; {h,n,z,v,c}
ADCB data       B = .B + data + .c; {h,n,z,v,c}
ADDA opnd       A = .A + .opnd; {h,n,z,v,c}
ADDA data       A = .A + data; {h,n,z,v,c}
ADDB opnd       B = .B + opnd; {h,n,z,v,c}
ADDB data       B = .B + data; {h,n,z,v,c}
ADDD opnd       (A|B) = .(A|B) + .opnd; {n,z,v,c}
ADDD data       (A|B) = .(A|B) + data; {n,z,v,c}
ANDA opnd       A = .A and .opnd; v = 0; {n,z,v}
ANDA data       A = .A and data; v = 0; {n,z,v}
ANDB opnd       B = .B and opnd; v = 0; {n,z,v}
ANDA data       B = .B and data; v = 0; {n,z,v}
ANDCC data8     CC = .CC and data8; {f,h,i,n,z,v,c}
ASL opnd        opnd = .opnd ash 1; {h,n,z,v,c}
ASLA            A = .A ash 1; {h,n,z,v,c}
ASLB            B = .B ash 1; {h,n,z,v,c}
ASR opnd        opnd = .opnd ash -1; {h,n,z,v,c}
ASRA            A = .A ash -1; {h,n,z,v,c}
                                                                           6809

                      CROSS-Microcomputer cross assembler                    50


ASRB            B = .B ash -1; {h,n,z,v,c}
BCC opnd        if not .c then BRA opnd;
BCS opnd        if .c then BRA opnd;
BEQ opnd        if .z then BRA opnd;
BGE opnd        if not (.n xor .v) then BRA opnd
BGT opnd        if not (.z or (.n xor .v)) then BRA opnd
BHI opnd        if not (.c xor .z) then BRA opnd
BHS opnd        if not .c then BRA opnd
BITA            .A and opnd; v = 0; {n,z,v}
BITB            .B and opnd; v = 0; {n,z,v}
BLE opnd        if .z or (.n xor .v) then BRA opnd
BLO opnd        if .c then BRA opnd
BLS opnd        if (.c or .z) then BRA opnd
BLT opnd        if (.n xor .v) then BRA opnd
BMI opnd        if .n then BRA opnd
BNE opnd        if not .z then BRA opnd
BPL opnd        if not .n then BRA opnd
BR
BRA
BRN             ;
BSR
BVC opnd        if not .v then BRA opnd;
BVS opnd        if .v then BRA opnd;
CLR opnd        opnd = 0; n = 0; z = 1; v = 0; c = 0; {n,z,v,c}
CLRA            A = 0; n = 0; z = 1; v = 0; c = 0; {n,z,v,c}
CLRB            B = 0; n = 0; z = 1; v = 0; c = 0; {n,z,v,c}
CMPA opnd       .A - .opnd; {h,n,z,v,c}
CMPB opnd       .B - .opnd; {h,n,z,v,c}
CMPB data       .B - data; {h,n,z,v,c}
CMPD opnd       .(A|B) - .opnd; {h,n,z,v,c}
CMPD data       .(A|B) - data; {h,n,z,v,c}
CMPS opnd       .S - .opnd; {n,z,v,c}
CMPS data       .S - data; {h,n,z,v,c}
CMPU opnd       .U - .opnd; {n,z,v,c}
CMPU data       .U - data; {h,n,z,v,c}
CMPX opnd       .X - .opnd; {n,z,v,c}
CMPX data       .X - data; {h,n,z,v,c}
CMPY opnd       .Y - .opnd; {n,z,v,c}
CMPY data       .Y - data; {h,n,z,v,c}
COM opnd        opnd = not .opnd; v = 0; c = 1; {n,z,v,c}
COMA            A = not .A; v = 0; c = 1; {n,z,v,c}
COMB            B = not .B; v = 0; c = 1; {n,z,v,c}
CPX
CWAI data8      e = 1; PSHS PC,U,Y,X,DP,B,A,CC; .CC and data8;} wait for
                interrupt {f,h,i,n,z,v,c}
DAA             bcd arithmetic adjust {n,z,v,c}
DEC opnd        opnd = .opnd -1; {n,z,v}
DECA            A = .A - 1; {n,z,v}
DECB            B = .B - 1; {n,z,v}
EORA opnd       A = .A xor .opnd; v = 0; {n,z,v}
EORA data       A = .A xor data; v = 0; {n,z,v}
EORB opnd       B = .B xor .opnd; v = 0; {n,z,v}
                                                                           6809

                      CROSS-Microcomputer cross assembler                    51


EORB data       B = .B xor data; v = 0; {n,z,v}
EXG r ,r        r  <=> r ; {h,f,i,n,z,v,c}
     1  2        1      2
INC opnd        opnd = .opnd + 1; {n,z,v}
INCA            A = .A + 1; {n,z,v}
INCB            B = .B + 1; {n,z,v}
JMP opnd        PC = opnd;
JSR
LBCC opnd       if not .c then LBRA opnd;
LBCS opnd       if .c then LBRA opnd;
LBEQ opnd       if .z then LBRA opnd;
LBGE opnd       if not (.n xor .v) then LBRA opnd;
LBGT opnd       if not (.z or (.n xor .v)) then LBRA opnd;
LBHI opnd       if not (.c xor .z) then LBRA opnd;
LBHS opnd       if not .c then LBRA opnd;
LBLE opnd       if .z or (.n xor .v) then LBRA opnd;
LBLO opnd       if .c then LBRA opnd;
LBLS opnd       if (.c or .z) then LBRA opnd;
LBLT opnd       if (.n xor .v) then LBRA opnd;
LBMI opnd       if .n then LBRA opnd;
LBNE opnd       if not .z then LBRA opnd;
LBPL opnd       if not .n then LBRA opnd;
LBR
LBRA
LBRN            ;
LBSR
LBVC opnd       if not .v then LBRA opnd;
LBVS opnd       if .v then LBRA opnd;
LDA opnd        A = .opnd; v = 0; {n,z,v}
LDA data        A = data; v = 0; {n,z,v}
LDAA            Synonym for LDA
LDAB            Synonym for LDB
LDB opnd        B = .opnd; v = 0; {n,z,v}
LDB data        B = data; v = 0; {n,z,v}
LDD opnd        (A|B) = (.opnd|.(opnd+1)); v = 0; {n,z,v}
LDD data16      (A|B) = data16; v = 0; {n,z,v}
LDS opnd        S = (.opnd|.(opnd+1)); v = 0; {n,z,v}
LDS data16      S = data16; v = 0; {n,z,v}
LDU opnd        U = (.opnd|.(opnd+1)); v = 0; {n,z,v}
LDU data16      U = data16; v = 0; {n,z,v}
LDX opnd        X = (.opnd|.(opnd+1)); v = 0; {n,z,v}
LDX data16      X = data16; v = 0; {n,z,v}
LDY opnd        Y = (.opnd|.(opnd+1)); v = 0; {n,z,v}
LDY data16      Y = data16; v = 0; {n,z,v}
LEAS opnd       S = opnd;
LEAU opnd       U = opnd;
LEAX opnd       X = opnd; {z}
LEAY opnd       Y = opnd; {z}
LSL opnd        opnd = .opnd lsh 1; {h,n,z,v,c}
LSLA            A = .A lsh 1; {h,n,z,v,c}
LSLB            B = .B lsh 1; {h,n,z,v,c}
LSR opnd        opnd = .opnd lsh -1; n = 0; {n,z,c}
                                                                           6809

                      CROSS-Microcomputer cross assembler                    52


LSRA            A = .A lsh -1; n = 0; {n,z,c}
LSRB            B = .B lsh -1; n = 0; {n,z,c}
MUL             (A|B) = .A * .B; {z,c}
NEG opnd        opnd = - .opnd; {h,n,z,v,c}
NEGA            A = - .A; {h,n,z,v,c}
NEGB            B = - .B; {h,n,z,v,c}
NOP             ;
ORA opnd        A = .A or .opnd; v = 0; {n,z,v}
ORA data        A = .A or data; v = 0; {n,z,v}
ORAA opnd       Synonym for ORA
ORAB opnd       Synonym for ORB
ORB opnd        B = .B or .opnd; v = 0; {n,z,v}
ORB data        B = .B or data; v = 0; {n,z,v}
ORCC data8      CC = .CC or data8; {f,h,i,n,z,v,c}
PSHS reglist    if PC in reglist then (S=.S-1; .S = .PC<0,8>; S=.S-1;
                .S=.PC<8,8>);
                if U in reglist then (S=.S-1; .S = .U<0,8>; S=.S-1;
                .S=.U<8,8>);
                if Y in reglist then (S=.S-1; .S = .Y<0,8>; S=.S-1;
                .S=.Y<8,8>);
                if X in reglist then (S=.S-1; .S = .X<0,8>; S=.S-1;
                .S=.X<8,8>);
                if DP in reglist then (S=.S-1; .S = .DP;)
                if B in reglist then (S=.S-1; .S = .B<0,8>;)
                if A in reglist then (S=.S-1; .S = .A;)
                if CC in reglist then (S=.S-1; .S = .CC;)
PSHU reglist    if PC in reglist then (U=.U-1; .U = .PC<0,8>; U=.U-1;
                .U=.PC<8,8>);
                if S in reglist then (U=.U-1; .U = .S<0,8>; U=.U-1;
                .U=.S<8,8>);
                if Y in reglist then (U=.U-1; .U = .Y<0,8>; U=.U-1;
                .U=.Y<8,8>);
                if X in reglist then (U=.U-1; .U = .X<0,8>; U=.U-1;
                .U=.X<8,8>);
                if DP in reglist then (U=.U-1; .U = .DP;)
                if B in reglist then (U=.U-1; .U = .B<0,8>;)
                if A in reglist then (U=.U-1; .U = .A;)
                if CC in reglist then (U=.U-1; .U = .CC;)
PULS reglist    if CC in reglist then (CC = .(.S); S=.S+1);
                if A in reglist then (A = .(.S); S=.S+1);
                if B in reglist then (B = .(.S); S=.S+1);
                if DP in reglist then (DP = .(.S); S=.S+1);
                if X in reglist then (X<8,8> = .(.S); S=.S+1;
                X<0,8> = .(.S); S=.S+1);
                if Y in reglist then (Y<8,8> = .(.S); S=.S+1;
                Y<0,8> = .(.S); S=.S+1);
                if U in reglist then (U<8,8> = .(.S); S=.S+1;
                U<0,8> = .(.S); S=.S+1);
                if PC in reglist then (PC<8,8>= .(.S); S=.S+1; PC<0,8> = .(.S);
                S=.S+1);
PULU reglist    if CC in reglist then (CC = .(.U); U=.U+1);
                if A in reglist then (A = .(.U); U=.U+1);
                                                                           6809

                      CROSS-Microcomputer cross assembler                    53


                if B in reglist then (B = .(.U); U=.U+1);
                if DP in reglist then (DP = .(.U); U=.U+1);
                if X in reglist then (X<8,8> = .(.U); U=.U+1;
                X<0,8> = .(.U); U=.U+1);
                if Y in reglist then (Y<8,8> = .(.U); U=.U+1;
                Y<0,8> = .(.U); U=.U+1);
                if S in reglist then (S<8,8> = .(.U); U=.U+1;
                S<0,8> = .(.U); U=.U+1);
                if PC in reglist then (PC<8,8>= .(.U); U=.U+1; PC<0,8> = .(.U);
                S=.S+1);
ROL opnd        c|opnd = .(c|opnd) rot 1;
ROLA            c|A = .(c|A) rot 1;
ROLB            c|B = .(c|B) rot 1;
ROR opnd        c|opnd = .(c|opnd) rot 1;
RORA            c|A = .(c|A) rot -1;
RORB            c|B = .(c|B) rot -1;
RTI
RTS
SBCA opnd       A = .A - .opnd - .C; {n,z,v,c}
SBCA data       A = .A - data - .C; {n,z,v,c}
SBCB opnd       B = .B - .opnd - .C; {n,z,v,c}
SBCB data       B = .B - data - .C; {n,z,v,c}
SEX             sign extend B into A; v = 0; {n,z,v}
STA opnd        opnd = .A; v = 0; {n,z,v}
STAA opnd       Synonym for STA
STAB opnd       Synonym for STB
STB opnd        opnd = .B; v = 0; {n,z,v}
STD opnd        opnd|opnd+1 = .(A|B); v = 0; {n,z,v}
STS opnd        opnd|opnd+1 = .S; v = 0; {n,z,v}
STU opnd        opnd|opnd+1 = .U; v = 0; {n,z,v}
STX opnd        opnd|opnd+1 = .X; v = 0; {n,z,v}
STY opnd        opnd|opnd+1 = .Y; v = 0; {n,z,v}
SUBA opnd       A = .A - .opnd; {n,z,v,c}
SUBA data       A = .A - data; {n,z,v,c}
SUBB opnd       B = .B - .opnd; {n,z,v,c}
SUBB data       B = .B - data; {n,z,v,c}
SUBD opnd       (A|B) = .(A|B) - .opnd|.(opnd+1); {n,z,v,c}
SUBD data       (A|B) = .(A|B) - data; {n,z,v,c}
SWI             software interrupt PSHS PC,U,Y,X,DP,B,A,CC; e=1; i=1; f=1;
                PC = ^HFFFA;
SWI2            software interrupt PSHS PC,U,Y,X,DP,B,A,CC; e=1; i=1; f=1;
                PC = ^HFFF4;
SWI3            software interrupt PSHS PC,U,Y,X,DP,B,A,CC; e=1; i=1; f=1;
                PC = ^HFFF2;
SYNC            synchronize
TFR r ,r        r  = r 
     1  2        2    1
TST opnd        .opnd - 0; v = 0; {n,z,v}
TSTA            .A - 0; v = 0; {n,z,v}
TSTB            .B - 0; v = 0; {n,z,v}


                                                                           6809

                      CROSS-Microcomputer cross assembler                    54


XI. Compiler directives
  The  following  compiler directives and their presumed meanings are described
briefly here.  This is only a  refresher  for  those  who  have  read  the  DEC
assembler description.

.ABS            Compile non-relocatable (absolute) code.

.ADDR           Generates  a  16-bit  address  with the bytes in swapped order,
                i.e., <low> <high>.  Equivalent  of  a  compile-time  byte-swap
                operation on a .WORD.

.ASCII          ASCII string delimited by paired markers.

.ASCIZ          ASCIZ  string  delimited  by  paired  markers and supplied with
                terminal null byte.

.ASECT          Not implemented in CROSS.

.BLKB           Allocate space for a  number  of  bytes  as  specified  by  the
                operand.

.BLKW           Allocate  space  for  a  number  of  words  as specified by the
                operand.

.BYTE           Each expression supplied will be stored in a single byte.

.CSECT          Not implemented in CROSS.

.DEPHA          Dephase; leave .PHASE control area.

.DSABL          See chapter 5.

.ENABL          See chapter 5.

.END            End of program.

.ENDC           End of conditional; paired with .IF.

.ENDM           End of macro definition or repeat; paired  with  .MACRO,  .IRP,
                .IRPC, .REPT.

.ENDR           End  of  repetition;  paired with .REPT; equivalent to .ENDM in
                this context.

.EOT            End-of-tape; assembler will wait for next  tape  to  be  loaded
                (paper tape hackers only).

.EQUIV          Equates two symbols:

                        .equiv defsym,anysym

                The symbols may be user symbols, builtin symbols, or macros.
                                                            Compiler directives

                      CROSS-Microcomputer cross assembler                    55


.ERROR          Causes  an error message to be issued.  The optional expression
                is evaluated and output if present.

                    label: .Print expr;text

.FLT2           ?

.FLT4           ?

.GLOBL          Not implemented in CROSS.

.IF
                Enter a conditional.

.IFDF           .IFDF <symbol> true if symbol is defined.  See also .IFNDF.

.IFEQ           .IFEQ <expression> true if expression evaluates to zero.

.IFF            Begins body of conditional if enclosing condition was false.

.IFG            .IFG <expression> true if expression greater than zero.

.IFGE           .IFGE <expression> true if expression greater than or equal  to
                zero.

.IFGT           Same as .IFG

.IFL            .IFL <expression> true if expression is negative.

.IFLE           .IFLE <expression> true if expression is negative or zero.

.IFLT           Same as .IFL.

.IFNDF          .IFNDF <symbol> true if symbol is undefined.

.IFNE           .IFNE <expression> true if expression is non-zero.

.IFNZ           Same as .IFNE

.IFT            Begins body of conditional if enclosing condition was true.

.IFTF           Text  from  here  to the next .IFT, .IFF or .IFTF or the end of
                the conditional will be included independent of  the  value  of
                the condition of the enclosing conditional.

.IFZ            Same as .IFE

.IIF condition, arg, stmnt
                Immediate if; if condition is met, stmnt is emitted.

.IRP            Indefinite repeat of the body; Sucessive arguments from arglist
                are assigned to sym.
                                                            Compiler directives

                      CROSS-Microcomputer cross assembler                    56


                        .IRP sym,arglist
                           body
                        .ENDR

.IRPC           Indefinite repeat of the body.  Successive characters of string
                are assigned to sym.

                        .IRPC sym,string
                           body
                        .ENDR

                .LIMIT
                Not implemented in CROSS.

.LIST           Enable listing.

.LOCAL          Not implemented in CROSS.

.MACRO          Begin a macro definition

                        .MACRO name arglist
                           body
                        .ENDM

.MCALL          Call macros from the system library.  See chapter 7.

.MEXIT          Leave macro expansion

.NARG sym       The symbol is equated to the number of arguments to the macro

.NCHR sym,str   The  symbol  sym  is equated to the number of characters in the
                delimited string str

.NLIST          Turn off listing

.NTYPE sym,arg  The symbol is equated to the addressing mode of the argument.

.PAGE           Force a page break

.PDP10          Irrelevant

.PHASE          Assemble code as if it were located according to  the  argument
                of this directive.

.PRINT          Print the text which follows on the terminal.

                    label: .Print expr;text

.PSECT          Not implemented in CROSS.

.RADIX          Change the radix to the value specified to this directive.

                                                            Compiler directives

                      CROSS-Microcomputer cross assembler                    57


.RAD50          Each   argument  is  converted  to  a  radix50  representation,
                according to the  PDP-11  radix50  conventions.    This  allows
                packing  three  bytes of compressed data in a 16-bit word. (The
                "50" is octal 50)

.REM            Include a remark

.REPT           (.REPT <n>) Repeat the body of  this  directive  the  indicated
                number of times.

.ROUND          Perform  arithmetic  operations with rounding to integer result
                (see also .TRUNC).

.SBTTL          Specify subtitle text.

.SETDP          (6809 only) Tells the assembler which page is  currently  being
                addressed by the Direct Page register; see page 49.  .TITLE
                Specify title text.

.TRUNC          Perform arithmetic operations with truncation to integer result
                (see also .ROUND)

.WORD           Allocate  space  for  each  value  specified.   Each expression
                evaluates to a word (16 bits).




























                                                            Compiler directives

                      CROSS-Microcomputer cross assembler                    58


XII. Macro quick summary

?               When  specified  with a formal, will cause a compiler-generated
                symbol to be provided  if  an  actual  is  not  given  in  that
                position.

'               Internal concatenation character

\<expr>         When  used  as  an argument, evaluates <expr> before performing
                the actual-formal match.










































                                                                  Macro summary

                      CROSS-Microcomputer cross assembler                    59


XIII. Assembler syntax quick summary

<...>           Encloses   any   expression   (the  assembler's  equivalent  of
                parentheses).  Expressions are evaluated left-to-right  without
                operator heirarchy.

+               Addition or unary plus

-               Subtraction or unary minus

*               Multiplication

/               Division

&               Logical and

!               Logical or

;               Begins comment field

'               Indicates single ASCII character as a term in expressions.

@               Indicates  octal  radix number; same as ^O prefix (not valid in
                8048 mode, where it is used to indicate addressing modes).

^B              Indicates binary number

^C              Takes the unary complement ("not") of the following expression

^H              Indicates hexadecimal number

^O              Indicates octal number

=               Symbol assignment

.               Current location counter

$               Indicates hexadecimal number

%               Indicates binary number (6502/6800/6805/6809 mode only)

^               If a postfix operator, divides the expression by 256.

\               If a postfix operator, takes the  evaluated  expression  modulo
                256 (low byte).







                                                              Assembler summary

                      CROSS-Microcomputer cross assembler                    60


XIV. Error codes

A               Addressing  error;  illegal  mode,  length  of  address, signed
                offset, etc.

D               Doubly-defined symbol referenced.

E               .end directive not found (its presence is assumed).

I               Illegal character detected,  i.e.,  a  non-printing  character;
                printed as ? in the listing file.

L               Line buffer overflow; input line too long.

M               Multiple definition of a label; remember that labels are unique
                only to the first 6 characters.

N               Number  error;  a  digit  not  legal  in  the  given  radix has
                appeared.

O               Opcode or directive error.

P               Phase error; a label has a different value between pass  1  and
                pass  2.    Possible causes are strange conditional expansions,
                phase conditionals, etc.  but note also that some  modes  which
                generate  "short"  and  "long" addresses may generate different
                lengths on different passes.  See the warnings on pages 44  and
                47.

Q               Questionable  syntax.    There are missing instructions, or the
                instruction scan was  not  completed,  or  a  comment  was  not
                properly delimited.

R               Register error; improper use of a register operand.

T               Truncation error; a value has more than 16 bits of significance
                in  a  16-bit context or more than 8 bits of significance in an
                8-bit context.

U               Undefined symbol.  The undefined symbol is assigned a value  of
                0.

Z               Instruction error. The instruction flagged may not be available
                on  the  destination  processor.  This warning occurs when z-80
                instructions are used without a .enable z80 directive.







                                                              Assembler summary

                      CROSS-Microcomputer cross assembler                    61


XV. Object format

XV.1. PTP object format
  If  the /PTP switch is given (and it must be given with the output file name,
not as part of the input file specification), the object  format  is  an  ASCII
file.    The details are determined by either the default output format derived
from the input file extension, or by the argument to the /PTP switch; see  page
5.



XV.1.1. COSMAC format



XV.1.2. INT Format
  This format is used by Intel, Mostek, and the CP/M operating system.

Leader:         One  character, a colon, indicating the start of a record.  All
                characters preceding the colon should be ignored.

Byte count:     Two characters (ASCII-encoded hex)  indicating  the  number  of
                data bytes in the record.  This byte count does not include the
                leader  character,  byte  count,  or address information.  Each
                data byte is  represent  by  two  characters,  this  is  not  a
                character count.

Address:        Four  characters  (ASCII-encoded  hex)  indicating the starting
                load address for the record.

Record Type:    Two characters, always 00, meaning an absolute block.  This  is
                00  even  in  blocks  that contain just a starting address. The
                starting address should be detected by  a  data  length  of  0,
                rather  than  the  record  type.  In  this format, the starting
                address is often given with record type 01. CROSS does  not  do
                this.

Data:           Several pairs of ASCII-encoded hex bytes to be loaded.

Checksum:       Two  characters  of (ASCII-encoded hex) checksum.  The checksum
                is the negated 8-bit sum  of  the  byte  count,  address  high,
                address  low, and data bytes, after they have been converted to
                binary.



XV.1.3. KIM Format

Leader:         One character, a semi-colon, indicating the start of a  record.
                All characters preceding the semi-colon should be ignored.

Byte count:     Two  characters  (ASCII-encoded  hex)  indicating the number of
                                                                  Object format

                      CROSS-Microcomputer cross assembler                    62


                data bytes in the record.  This byte count does not include the
                leader  character,  byte  count,  or address information.  Each
                data byte is  represent  by  two  characters,  this  is  not  a
                character count.

Address:        Four  characters  (ASCII-encoded  hex)  indicating the starting
                load address for the record.

Data:           Several pairs of ASCII-encoded hex bytes to be loaded.

Checksum:       Four characters of (ASCII-encoded hex) checksum.  The  checksum
                is  the  negated  16-bit  sum  of the byte count, address high,
                address low, and data bytes, after they have been converted  to
                binary.



XV.1.4. MOT Format
  This  format uses the S1 and S9 records of the standard Motorola format.  The
S1 record is a data record, and consists of:  

S1              The characters which indicate the record type.

Byte count      Two characters of byte  count  (ASCII-encoded  hex);  the  byte
                count  is  the count of all following data bytes, including the
                checksum.

Address         Four characters (ASCII-encoded hex) indicated the starting load
                address for the record.

Data            Two characters of ASCII-encoded hex for each byte to be loaded.

Checksum        A two character (one byte, ASCII-encoded hex) checksum  of  the
                binary  values of the byte count, address, and data bytes.  The
                sum of all these bytes plus the checksum should equal FF  .
                                                                        16
  An S9 record is a transfer record, and consists of:  

S9              The record type indicator

Byte count      Same as an S1 record.

Address         Four characters (two bytes  ASCII-encoded  hex);  the  transfer
                address at which exection should begin; if there was no address
                on the .end statement, the value 0 is assumed.

Checksum        Same as an S1 record.

XV.2. Binary file formats



                                                                  Object format

                      CROSS-Microcomputer cross assembler                    63


XV.2.1. Packed binary file format

+---+---------------+---------------+---+---------------+---------------+
|///|  byte 2       |    byte 1     |///|    byte 4     |    byte 3     |
|///|               |               |///|               |               |
+---+---------------+---------------+---+---------------+---------------+
 0 1 2 3 4 5 6 7 8 9 1 1 1 1 1 1 1 1 1 1 2 2 2 2 2 2 2 2 2 2 3 3 3 3 3 3
                     0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5

                                    2
  This  is  the "packed" output mode .  The bytes must first be serialized, and
then interpreted according to the description given in section XV.2.3.



XV.2.2. Image binary file format
  The image binary output form consists of one 8-bit byte in  the  low-order  8
bits  of a PDP-10 word.  Word 0 of the output file is the first byte, word 1 of
the output file is the second  byte,  etc.    The  bytes  must  be  interpreted
according to the description given in section XV.2.3.



XV.2.3. Object format
  After  obtaining  a  serial  byte stream from either a packed or image binary
file, the bytes are interpreted as:  

   - some number (zero or more) of 0 bytes (discard)

   - a byte with the value 1.  (This byte is counted in the checksum).

   - a byte with the value 0.  (This byte is counted in the checksum,  but
     of course it has no effect because it is 0).

   - The  low-order  8  bits  of the byte count, which we will refer to as

     BC .
       L
   - The high-order 8 bits of the byte count, which we will  refer  to  as

     BC .  The byte count BC is thus computed by
       H
                 BC = (BC  * 400 ) + BC 
                         H      8      L

               

  2
   If  you  stare  at  this and squint your eyes a bit, you will see that it is
laid down as two PDP-11 words; the first word is in the left  PDP-10  halfword,
so  the  lower-addressed byte is to the right.  The second word is in the right
PDP-10 halfword.
                                                                  Object format

                      CROSS-Microcomputer cross assembler                    64


   - The  low-order 8 bits of the address where the data will go, which we
     will refer to as A .  This byte is counted as part of BC.
                       L
   - The high-order 8 bits of the address where the data will go, which we
     will refer to as A .  This byte is counted as part of BC.   The  load
                       H
     address A is computed as the byte count, i.e.,

         A = (A  * 400 ) + A 
               H      8     L
   - BC-6  bytes of data, in order, starting with the byte for the address
     A, then A+1, A+2, etc.

   - One byte of checksum, which is the complemented sum of all the bytes.
     When all of the bytes starting at the constant 1  plus  the  checksum
     are added, the result should be zero.

The  above  is  repeated  as often as required to load the data.  The last such
group has BC=6 and the starting address is A.  Thus, it contains no data bytes.
This is the only way to distinguish this "transfer  address"  record  from  any
other record.































                                                                  Object format

                      CROSS-Microcomputer cross assembler                    65


XVI. Site-specific differences
  The  CROSS program can be configured for various sites.  It is suggested that
if you wish to make site-specific changes, you make  them  in  a  copy  of  the
master  copy of the source, which currently resides at <MicroComputer>@Rutgers.
Use conditional compilation switches, and when you are done, contact Rutgers to
take your source  back.    In  this  way,  we  have  the  advantage  of  shared
maintenance.

  Please  contact  Joe Newcomer (Newcomer@CMU-10A) for up-to-date documentation
sources.

  The current site-dependent configuration switches are:

CMUASW          Uses CMU PPN format for CMU TOPS-10 systems

CMUSW           Looks for SWITCH.INI on device HOM: first.

                Sets default page length and width for the Dover printer  using
                SAILA8.

UTAHSW          Uses [4,156], <Micro>, as the PPN for .MCALL libraries.































                                                                  Object format

                      CROSS-Microcomputer cross assembler                    66


Index

          !   59

          #, in cref   9

          $<expr>   1, 59

          %<expr>   1, 59
          %nn, register   1

          &   59

          ', concatenation   58, 59

          *   59
          *, in cref   9

          +   59

          -   59

          ., location counter   59
          .ABS   54
          .ADDR   54
          .ASCII   54
          .ASCIZ   54
          .ASECT   54
          .BLKB   54
          .BLKW   54
          .BYTE   54
          .CSECT   54
          .DEPHAse   54
          .DSABL   5, 12, 54
          .ENABL   4, 12, 54
          .END   54
          .ENDC   54
          .ENDM   54
          .ENDR   54
          .EOT   54
          .EQUIV   54
          .ERROR   54
          .FLT2   55
          .FLT4   55
          .GLOBL   55
          .IF   55
          .IFDF   55
          .IFEQ   55
          .IFF   55
          .IFG   55
          .IFGE   55
          .IFGT   55
                                                                          Index

                      CROSS-Microcomputer cross assembler                    67


          .IFL   55
          .IFLE   55
          .IFLT   55
          .IFNDF   55
          .IFNE   55
          .IFNZ   55
          .IFT   55
          .IFTF   55
          .IFZ   55
          .IIF   55
          .IRP   55
          .IRPC   56
          .LIMIT   56
          .LIST   4, 7, 8, 56
          .LOCAL   56
          .MACRO   56
          .MCALL   14, 56
          .MEXIT   56
          .NARG   56
          .NCHR   56
          .NLIST   4, 7, 8, 56
          .NTYPE   56
          .PAGE   56
          .PDP10   56
          .PHASE   56
          .PRINT   56
          .PSECT   56
          .RAD50   56
          .RADIX   56
          .REM   57
          .REPT   57
          .ROUND   12, 57
          .SBTTL   57
          .SETDP   49, 57
          .TITLE   57
          .TRUNC   12, 57
          .WORD   57

          /   59
          /CDR   5
          /CRF   5, 9
          /DS   5, 12
          /EN   4, 12
          /EQ   6
          /GNS   6, 10
          /I   5
          /LEN   6, 10
          /LI   4, 8
          /M05   4
          /M08   4
          /M18   4
          /M48   4
                                                                          Index

                      CROSS-Microcomputer cross assembler                    68


          /M65   4
          /M68   4
          /M69   4
          /M80   4
          /M88   4
          /MF8   4
          /N   5, 9
          /NL   4, 8
          /NSQ   6
          /OCT   5, 9
          /P   5
          /PTP   5
          /SOL   6, 10
          /WID   6, 11

          1802   4, 34

          3870   4

          6502   4, 37
          6800   4, 40
          6805   4, 44
          6809   4, 47

          72, column   5

          8008   4, 28
          8048   4, 30
          8080   4, 17
          8085   4

          ;, comment delimiter   59

          <...>   59

          =   59

          ?, macro argument modifier   58

          @, in command   3
          @<expr>   1, 59, 1, 59

          .ABS   54
          ABS   12
          Absolute memory addressing   12
          .ADDR   54
          AMA   12
          And, assembler operator   59
          .ASCII   54
          .ASCIZ   54
          .ASECT   54

                                                                          Index

                      CROSS-Microcomputer cross assembler                    69


          ^B<expr>   1
          <expr>\   1
          \<expr>   58
          ^B<expr>   59
          <expr>\   59
          BEX, listing option   7
          BIN
             extension   3
             listing option   7
          Binary listing option   7
          Binary radix   1
          .BLKB   54
          .BLKW   54
          .BYTE   54
          Byte
             high   1
             Low   1, 59

          ^C<expr>   59
          Card reader simulation   5
          Catenation   15
          CCL file   3
          /CDR   5
          CMUSW   65
          CND, listing option   7
          COM, listing option   7
          Command line   3
          Comment
             delimiter   59
             listing option   7
          Concatenation operator   58, 59
          Conditional
             compilation: .IF   55
             listing option   7
          Contents, listing option   8
          COSMAC
          COSMAC 1802   4, 34
             Format   61
               See also   1802
          /CRF   5, 9
          CRF.TMP file   9
          Cross-reference   5
          .CSECT   54
          Current location counter   59

          D<expr>   1, 59
          Decimal radix   1
          .DEPHAse   54
          /DS   5, 12
          .DSABL   5, 12, 54
          DSK, device   3

                                                                          Index

                      CROSS-Microcomputer cross assembler                    70


          /EN   4, 12
          .ENABL   4, 12, 54
          .END   54
          .ENDC   54
          .ENDM   54
          .ENDR   54
          .EOT   54
          /EQ   6
          .EQUIV   54
          ERF   12
          .ERROR   54
          Error flags, suppression   12
          Error message suppression   5
          Exorcisor Format   5, 62
          $<expr>   1, 59
          %<expr>   1, 59
          @<expr>   1, 59
          ^B<expr>   1, 59
          ^C<expr>   59
          ^H<expr>   1, 59
          ^O<expr>   1, 59
          <expr>\   1
          \<expr>   58
          <expr>\   59
          <expr>^   1, 59
          Extension
             .BIN   3
             .CCL   3
             .LST   3
             .M05   3
             .M08   4
             .M18   4
             .M48   3
             .M65   4
             .M68   4
             .M69   4
             .M80   4
             .M88   4
             .MF8   4
             .SML   14

          F8   4
          Fairchild
             F8   4
          Floating point truncation   12
          .FLT2   55
          .FLT4   55
          Formats
             COS   5, 61
             COSMAC   5, 61
             CP/M   5, 61
             Exorcisor   5, 62
                                                                          Index

                      CROSS-Microcomputer cross assembler                    71


             Image binary   63
             INT   5, 61
             Intel   5, 61
             Intellec   5, 61
             KIM   5, 61
             MOS   5
             MOS Technology   5, 61
             Mostek   61
             MOT   5, 62
             Motorola   5, 62
             Packed binary   63
             PTP   61
          FPT   12

          Generate new source   6, 10
          .GLOBL   55
          /GNS   6, 10

          ^H<expr>   1, 59
          Hex output   5, 61, 62
          Hexadecimal radix   1
          High byte   1

          /I   5
          .IF   55
          .IFDF   55
          .IFEQ   55
          .IFF   55
          .IFG   55
          .IFGE   55
          .IFGT   55
          .IFL   55
          .IFLE   55
          .IFLT   55
          .IFNDF   55
          .IFNE   55
          .IFNZ   55
          .IFT   55
          .IFTF   55
          .IFZ   55
          .IIF   55
          Image mode output   5
          Intel
             8008   4, 28
             8048   30
             8080   4, 17
             8085   4
             MCS-48   4, 30
          .IRP   55
          .IRPC   56

          KIM
                                                                          Index

                      CROSS-Microcomputer cross assembler                    72


             Format   5, 61
               See also   6502

          LC   12
          LD, listing option   8
          /LEN   6, 10
          /LI   4, 8
          Libraries, macro   14
          .LIMIT   56
          Line numbers   6
          .LIST   4, 7, 8, 56
          Listing option
             BEX   7
             BIN   7
             CND   7
             COM   7
             LD   8
             LOC   7
             MB   7
             MC   7
             MD   7
             ME   7
             SEQ   7
             SRC   7
             SYM   8
             TOC   8
             TTM   8
          LOC, listing option   7
          .LOCAL   56
          Location counter   59
          Low byte   1, 59
          Lower case   12
          LPT, device   3
          LSB   12
          LST, extension   3

          M05
             /M05 switch   4
             extension   3
          M08
             /M08 switch   4
             extension   4
          M18
             /M18 switch   4
             extension   4
          M48
             /M48 switch   4
             extension   3
          M65
             /M65 switch   4
             extension   4
          M68
                                                                          Index

                      CROSS-Microcomputer cross assembler                    73


             /M68 switch   4
             extension   4
          M69
             /M69 switch   4
             extension   4
          M80
             /M80 switch   4
             extension   4
          M85   12
          M88
             /M88 switch   4
             extension   4
          .MACRO   56
          Macro call listing option   7
          Macro definition   56
          Macro libraries   14
          Macro, concatenation   58, 59
          MB, listing option   7
          MC, listing option   7
          .MCALL   14, 56
          MCS-48   4, 30
          MD, listing option   7
          ME, listing option   7
          Memory addressing, absolute   12
          .MEXIT   56
          MF8   4
             extension   4
          MOS Technology
             6502   4, 37
          Mostek
             3870   4
          Motorola
             6800   4, 40
             6805   4, 44
             6809   4, 47

          /N   5, 9
          .NARG   56
          .NCHR   56
          New source, generation   6, 10
          /NL   4, 8
          .NLIST   4, 7, 8, 56
               See also   ^C
          /NPP   12
          /NSQ   6
          .NTYPE   56

          ^O<expr>   1, 59
               See also   Formats
          /OCT   5, 9
          Octal radix   1, 5
          Or, assembler operator   59
                                                                          Index

                      CROSS-Microcomputer cross assembler                    74


          Output format   5

          /P   5
          %<expr>   1, 59
          Packed binary output   5
          .PAGE   56
          .PDP10   56
          .PHASE   56
          Phase error   47
          .PRINT   56
          .PSECT   56
          /PTP   5
          PTP, device   3
          PTR, device   3

          .RAD50   56
          .RADIX   56
          Radix
             10   1
             16   1
             2   1
             8   1, 5
             binary   1
             decimal   1
             default   1
             hexadecimal   1
             octal   1
          RCA
             1802   4, 34
          REG   12
          Register %nn   1
          .REM   57
          .REPT   57
          RIM, opcode   12
          Rockwell
             6502   37
          .ROUND   12, 57

          S1 record   62
          S9 record   62
          .SBTTL   57
          SEQ, listing option   7
          .SETDP   49, 57
          SIM, opcode   12
          Site-dependent
             CMU   65
             Utah   65
          /SOL   6, 10
          Source listing option   7
          Source, new, generation   6, 10
          SRC, listing option   7
          Suppression of error flags   12
                                                                          Index

                      CROSS-Microcomputer cross assembler                    75


          Switch
             CDR   5
             CRF   5, 9
             DS   5, 12
             EN   4, 12
             EQ   6
             GNS   6, 10
             I   5
             LEN   6, 10
             LI   4, 8
             M05   4
             M08   4
             M18   4
             M48   4
             M65   4
             M68   4
             M69   4
             M80   4
             M88   4
             N   5, 9
             NL   4, 8
             NPP   12
             NSQ   6
             OCT   5, 9
             P   5
             PTP   5
             SOL   6, 10
             WID   6, 11
          SWITCH.INI   13
          SYM, listing option   8
          Symbol table listing option   8
          Synertek
             6502   37
          SYSMAC.SML   14

          Table of contents, listing option   8
          Terminal format listing option   8
          TIM   12
          .TITLE   57
          TOC, listing option   8
          .TRUNC   12, 57
          Truncation   12
          TTM, listing option   8
          TTY, device   3

          <expr>^   1, 59
          UTAHSW   65

          /WID   6, 11
          .WORD   57

          Z80   4, 12, 21
                                                                          Index

                      CROSS-Microcomputer cross assembler                    76


          Z80 transliteration   23
          Zilog
             Z80   4, 21

          \, macro argument modifier   58
          \<expr>   58
          <expr>\   59

          <expr>^   1
          ^<expr>   59
          ^B<expr>   1, 59
          ^C<expr>   59
          ^H<expr>   1, 59
          ^O<expr>   1, 59

          |   15




































                                                                          Index

                      CROSS-Microcomputer cross assembler                     i


                               Table of Contents

1. Introduction                                                               1

2. Syntax differences                                                         2

3. Operating procedures                                                       3

3.1. Loading CROSS                                                            3
3.2. Initial dialogue                                                         3

4. Listing control                                                            7

4.1. Source statement listing control                                         7
4.2. Command string equivalents                                               8
4.3. Other listing controls                                                   9

5. Enable/Disable control                                                    12

6. User-defined switch defaults                                              13

7. Macro libraries                                                           14

I. General notation                                                          15

I.1. Machine State                                                           15
I.2. Notation                                                                15
I.3. Syntax                                                                  15
I.4. Opcodes                                                                 15

II. 8080 syntax                                                              17

II.1. Machine State                                                          17
II.2. Notation                                                               17
II.3. Syntax                                                                 18
II.4. Opcodes                                                                18

III. Z80 syntax                                                              21

III.1. Introduction                                                          21
III.2. Machine State                                                         21
III.3. Notation                                                              21
III.4. Opcodes                                                               21
III.5. Z80 Transliterations                                                  23

IV. 8008                                                                     28






                                                                          Index

                      CROSS-Microcomputer cross assembler                    ii


IV.1. 8080 subset                                                            28

V. 8048                                                                      30

V.1. Machine State                                                           30
V.2. Notation                                                                30
V.3. Syntax                                                                  31
V.4. Opcodes                                                                 31

VI. 1802                                                                     34

VI.1. Machine State                                                          34
VI.2. Opcodes                                                                34

VII. 6502                                                                    37

VII.1. Machine state                                                         37
VII.2. Notation                                                              37
VII.3. Syntax                                                                38
VII.4. Opcodes                                                               38

VIII. 6800                                                                   40

VIII.1. Machine State                                                        40
VIII.2. Notation                                                             40
VIII.3. Syntax                                                               41
VIII.4. Opcodes                                                              41

IX. 6805                                                                     44

IX.1. Machine State                                                          44
IX.2. Notation                                                               44
IX.3. Syntax                                                                 44
IX.4. Opcodes                                                                45

X. 6809                                                                      47

X.1. Machine State                                                           47
X.2. Notation                                                                48
X.3. Syntax                                                                  48
X.4. Opcodes                                                                 49

XI. Compiler directives                                                      54

XII. Macro quick summary                                                     58

XIII. Assembler syntax quick summary                                         59





                                                                          Index

                      CROSS-Microcomputer cross assembler                   iii


XIV. Error codes                                                             60

XV. Object format                                                            61

XV.1. PTP object format                                                      61
     XV.1.1. COSMAC format                                                   61
     XV.1.2. INT Format                                                      61
     XV.1.3. KIM Format                                                      61
     XV.1.4. MOT Format                                                      62
XV.2. Binary file formats                                                    62
     XV.2.1. Packed binary file format                                       63
     XV.2.2. Image binary file format                                        63
     XV.2.3. Object format                                                   63

XVI. Site-specific differences                                               65

Index                                                                        66



































                                                                          Index