107/10/84                                                             KERMIT-TSO



 1. Introduction

 KERMIT  is  a set of programs that transfer files between computers over normal
 terminal communication lines.  It implements the  "KL10  Error-Free  Reciprocol
 Microcomputer  Interchange over TTY-Lines" protocol.  Originally designed to be
 used between a microcomputer and the DEC-20, the protocol  will  also  transfer
 files  to  and  from  a  microcomputer  and IBM mainframe systems running under
 MVS/TSO.

 KERMIT transfers data by creating packets with information regarding  the  type
 of packet being sent, it's length, a packet number, and a checksum to determine
 whether the data has been modified during transmission.  If a packet is lost or
 garbled, KERMIT will attempt to resend it.

 Written  in  IBM  370  assembly language to run under MVS/TSO on IBM 370-series
 mainframes (System/370, 303x, 43xx, 308x, ...). These are half duplex  systems;
 the  communication  line  must "turn around" before any data can be sent to it.
 The fact that a packet has been received from the IBM system  is  no  guarantee
 that it is ready for a reply.  Thus any Kermit talking to this system must wait
 for the line turnaround character (XON) before transmitting the next character.

 IBM  systems  talk  to  their terminals through a communications front end (IBM
 3705, 3725, COMTEN 3670, etc).  These front ends generally insist on using  the
 8th  bit  of  each  character  for parity.  This means that binary files (files
 con-taining other than ordinary letters, digits, punctuation, carriage returns,
 tabs, and so forth) can not be correctly sent or received by these systems with
 Kermit (protocol version 1).

 The IBM system under MVS/TSO is unable to interrupt a read  on  its  "console".
 This  means  that  the  IBM  version of Kermit cannot timeout.  The only way to
 "timeout" TSO Kermit is from the other side -- typing a carriage return to  the
 micro's  Kermit  causing  it  to  retransmit  its  last packet, or an automatic
 timeout as provided by Kermit-20.  For this reason,  TSO  Kermit  waits  thirty
 seconds  before sending its first packet when sending files from MVS/TSO.  This
 gives the user sufficient time to return to the  local  Kermit  and  issue  the
 Receive  command.   Otherwise, a protocol deadlock would arise requiring manual
 intervention by the user.

 Also, MVS/TSO stores files as records rather byte streams.  MVS/TSO Kermit  has
 to  worry  about  assembling  incoming  data packets into records and stripping
 CRLFs from incoming lines, and also appending CRLFs to - and stripping trailing
 blanks from -- outgoing records.

 You must be using an ASCII terminal to run KERMIT-TSO.

 KERMIT-TSO must be installed as a Command Processor (CP) on your system.

 Please note that this document should be used in conjunction  with  the  Kermit
 manual,  and  assumes  you  have  read  the  sections  pertaining to the IBM/PC
 microcomputer.  For more information regarding the manual,  see  the  Reference
 section at the end of this report.
-
0
                                      -1-
107/10/84                                                             KERMIT-TSO



 2. TSO Command Syntax and Options


 KERMIT


 You simply type a carriage return after issuing the
 KERMIT command.

 Commands:

           Send

           Receive

           Set

           Show

           Status

           Help

           Exit

           Quit

           ?

 2.1. TSO KERMIT Command Options

 SEND [dataset name]
                Send the specified dataset.  KERMIT-TSO will send
                only  one  file  per  request,  no wildcarding is
                allowed.  If the dataset name is  not  specified,
                KERMIT-TSO  will  prompt  for one.  Note, dataset
                must be cataloged.

 RECEIVE [dataset name]
                Receive the file sent from  the  micro.   If  the
                dataset  name  is  not  specified KERMIT-TSO will
                prompt for one.  If no dataset previously  exists
                with  this  name a file will be created using the
                value of the SPACE  parameter.   (NOTE,  at  this
                time  KERMIT-TSO does not trap for abends, and if
                the  file  being  received  excedes   the   space
                allocated  KERMIT-TSO will abnormally terminate.)
                The attributes for the dataset will be taken from
                the RECFM, LRECL, and BLKSIZE parameters.   If  a
                dataset  exists  KERMIT-TSO will prompt to see if
                you wish to overwrite the dataset.

 SET <parameter> <value>
                Set the parameter to the specified value.   Legal
                Set commands are:

                                      -2-
107/10/84                                                             KERMIT-TSO



                SPACE <d>
                     Specifies   the   number  of  tracks  to  be
                     allocated to the dataset.  The default is  5
                     tracks.   Both  the  primary  and  secondary
                     allocation are set to the value specified.

                RECFM <c>
                     Denotes the record format to  be  used  when
                     creating   the   dataset.   Only  fixed  and
                     variable length records are  allowed,  where
                     variable   is  the  default.   Indicate  the
                     desired record format by either an F or a V.

                BLKSIZE <d>
                     Indicates the block size  for  creating  the
                     dataset.   The default is 80 and the maximum
                     is 32767.  If the RECFM is F  the  blocksize
                     must be a multiple of the value specified in
                     the LRECL parameter.  If RECFM is F then the
                     BLOCKSIZE must be at least LRECL + 4.

                LRECL <d>
                     Indicates  the  logical  record  length  for
                     creating the dataset.  The default is set to
                     80, and the maximum allowed is 255.  If  the
                     RECFM  is  V  the  value  must include the 4
                     bytes for the record descriptor word (RDW).

                QUOTE <c>
                     The quote character you wish to use in place
                     of the default (#).  It must  be  a  single,
                     printable    character    from   among   the
                     following:  33-62, 96, or 123-126 (decimal).

                START <d>
                     Indicates  the   start-of-header   character
                     which  you  choose to send and receive.  The
                     default is a CNTL-A (ASCII 01), but  can  be
                     set  to  any two digit number between 00 and
                     31 (dec).

                END <d>
                     Indicates  the  end-of-line  character   you
                     choose  to send.  The default is a CR (ASCII
                     13), but can be set to any two digit  number
                     between 00 and 31 (dec).

                PAC <d>
                     Allows  the  user to specify the packet size
                     the  micro  should  use  when   sending   to
                     KERMIT-TSO.   The  range is 26-94 (decimal),
                     where 94 is the default.

                DEBUG [ON | OFF]
                     Allows the user to specify whether  a  trace

                                      -3-
107/10/84                                                             KERMIT-TSO



                     of  packet  information  will be writen to a
                     dataset.  Before using this option the  user
                     must  have  allocated a dataset to file name
                     (ddname) "DEBUG".

                DELAY <d>
                     Allow the user to specify the length of time
                     in seconds that KERMIT-TSO will  wait  after
                     the  user  issues a SEND.  The default is 20
                     seconds.  This will give the  user  time  to
                     escape  back  to  his micro KERMIT and issue
                     the neccesary commands.

 SHOW STATUS
                Displays the current value of all variables  that
                can be changed via the SET command.
 STATUS
                Returns  the  status of the previous execution of
                KERMIT-TSO.   Therefore,   STATUS   will   either
                display    the    message    "Kermit    completed
                successfully",  or  the  last  error  encountered
                prior to aborting.

 HELP           Displays a message that briefly explains KERMIT-TSO commands.

 EXIT           from KERMIT-TSO.

 QUIT           Same as EXIT.

 ?              Lists all legal KERMIT-TSO commands.


 3. Examples under TSO

 Here is a brief example of how to use the IBM/PC in conjunction with KERMIT-TSO
 to send a file to the IBM-PC.

     A>kermit

     Kermit-86>set loc on            ; Indicate half duplex
     Kermit-86>set ibm on            ; Cause line turn around wait
     Kermit-86>set baud 1200         ; Set the baud rate
     Kermit-80>connect

        [ The micro will act as a regular terminal from now on.]
        [ Login here as you normally would, and run KERMIT-TSO.]

     kermit
     KERMIT-TSO>?
     Legal Commands are:
     Receive, Send, Help, Exit, Quit, Set, Status, Show
     KERMIT-TSO>send finger.database         ; Send this file

     Waiting    20 seconds before sending.
     ^]C                                     ; Return to the micro

                                      -4-
107/10/84                                                             KERMIT-TSO



                                             ; by typing <escape>]C

     Kermit-86>
     Kermit-86>receive                       ; Micro receives the file

         [the file is sent .......]

     Kermit-86>connect

         [press carriage return to see TSO's prompt]

     KERMIT-TSO>status
     Kermit completed successfully
     KERMIT-TSO>ex
     READY
     logoff
     CONNECT TIME -  2:30.95
     SYSRONR Logged off TSO at 15:34:25 on July 6, 1984

     ^]C                         ; Return to the micro
                                 ; by typing <escape>C

     Kermit-86>exit
     A>

 In  order  to send a file from the IBM/PC to the IBM mainframe repeat the above
 procedure swapping the command SEND with RECEIVE and vice versa.


 4. Additional Information

    1. The  commands  are supplied with a help option, so a question mark can be
       typed to get the appropriate format or a list of options.   The  question
       mark,  however,  must  be  followed by a carriage return; KERMIT-TSO will
       respond and display the prompt again.  For instance, SET ?  will list all
       valid options for the SET command.

    2. When receiving files, if the record format is fixed,  any  record  longer
       than  the logical record length will be truncated.  The record length can
       be as high as 255.  For receiving files, the  maximum  record  length  is
       255.

    3. Before  connecting  to  the  IBM mainframe, three flags must be set.  You
       should set the IBM flag on, set the LOCAL-ECHO flag on (used to  indicate
       half  duplex),  and  specify  the baud rate you will be using.  To turn a
       flag on, type to the micro's prompt "Set XXX On" where XXX  is  the  flag
       name.  Indicate the baud rate by typing "Set baud", and choose from among
       a list the IBM-PC supplies.  These flags will remain in effect as long as
       you do not exit from the micro's version of Kermit.  See the example of a
       session for further clarification.

    4. The  current  version of KERMIT-TSO does not support timeouts.  The user,
       therefore, should hit the carriage return key  after  a  long  period  of
       inactivity (that is, when the screen display does not change.)


                                      -5-
107/10/84                                                             KERMIT-TSO



    5. Since  the micro does not send an error packet when it aborts, KERMIT-TSO
       does not know the micro has stopped sending it  information.   Therefore,
       when you connect back to the IBM, KERMIT-TSO may still be sending packets
       (they  will  appear  on the screen).  The user must hit a carriage return
       until KERMIT-TSO has sent the  maximum  number  of  packets  allowed  and
       aborts.  The error message, however, will not indicate that communication
       stopped  because  the  micro  aborted, but rather that no start of header
       character was found.

    6. The minimum send packet size  KERMIT-TSO  will  allow  is  26.   This  is
       necessary  to  avoid  an  error  while  sending  the filename or an error
       packet.  If the micro tries  to  set  the  value  to  be  less  than  26,
       KERMIT-TSO  will  immediately  abort  with  an  error of "Bad send-packet
       size."

    7. During the initialization process with the micro,  KERMIT-TSO  sends  all
       six  pieces of information (that is, the receive packet size, the timeout
       data, the number of padding characters, the character used  for  padding,
       the  line  terminator, and the quote character.) When receiving this data
       from the micro,  KERMIT-TSO  ignores  the  data  regarding  timeouts  and
       padding;  they  do not effect the program's execution.  Therefore, if the
       quote and end-of-line characters used are the defaults,  the  micro  need
       only  send KERMIT-TSO its buffer size.  Only if the defaults are not used
       must  ALL  the  information  be  sent  (since  the  data   is   organized
       positionally).   If,  however,  the  micro sends all the information even
       when not required, KERMIT-TSO will simply ignore the irrelevant portion.

    8. When sending packets to KERMIT-TSO, the micro must use a carriage  return
       as  the  end-of-line  character.   TSO  requires  a  carriage  return  to
       terminate a read from the terminal; thus, if any other character is used,
       KERMIT-TSO will never get the packets.

    9. KERMIT-TSO translates the data it reads back  to  ASCII  (characters  not
       representable in ASCII are replaced by a null).  Not only is it easier to
       work   with  ASCII  characters,  but  it  makes  things  more  consistent
       throughout the many versions of Kermit.  When the packets are sent to the
       micro, KERMIT-TSO converts all data back to EBCDIC.  The ASCII to  EBCDIC
       translation table can be found in Appendix V of the Kermit manual.

 4.1. Error Messages

 KERMIT-TSO  supplies  the  micro and the user with numerous error messages.  If
 the execution must be aborted, an error packet is  sent  to  the  micro  before
 KERMIT-TSO  stops.   The  same  message can be retrieved via the STATUS command
 when KERMIT-TSO returns and displays the prompt.  If KERMIT-TSO aborted because
 the maximum amount of retries was exceeded (20 on initialization packets and  5
 on  others),  the  error message will display the most recent error (i.e. - the
 last NAK  KERMIT-TSO  encountered).   If  execution  stops  because  the  micro
 aborted,  the error message will convey that to the user, but it is the micro's
 responsibility to pinpoint the error.  The messages  KERMIT-TSO  gives  are  as
 follows :

       "Bad send-packet size"
               Sent  when the micro attempts to set its receive buffer size to a
               value that is less than 26  (the  minimum  that  KERMIT-TSO  will

                                      -6-
107/10/84                                                             KERMIT-TSO



               accept)  or  larger  than 94, the maximum.  It will also occur if
               KERMIT-TSO tries to send a packet that is larger than the maximum
               specified.

       "Bad message number"
               If the packet number is less than zero or  greater  than  63  (at
               which point it should "wrap around" back to zero).


               This message is returned if the packet type does not fall between
               A-Z.

       "Unrecognized State"
               If  KERMIT-TSO  is  in  a  state  not  previously  defined by the
               protocol, it will abort with this message.

       "No SOH encountered"
               This error arises if KERMIT-TSO reads the entire  packet  without
               encountering an SOH character.  The result is that it sends a NAK
               to the micro, and marks this error as the most recent one.

       "Bad Checksum"
               If  the  checksum calculated by KERMIT-TSO does not match the one
               sent by the micro, KERMIT-TSO NAK's the  packet  and  flags  this
               error.

       "Bad character count"
               This  error  is set if KERMIT-TSO receives a packet whose size is
               illegal (that is,  if  the  size  parameter  was  garbled  during
               transmission of the packet.)

       "Micro sent a NAK"
               Keep track of who rejected the packet.

       "Lost a packet"
               When  a  packet  is received and the sequence number is different
               from the number KERMIT-TSO expected, the packet is NAK'ed.

       "Micro aborted"
               Tells you that the micro aborted unexpectedly.

       "Invalid RECFM, only fixed or variable supported"
               KERMIT-TSO will abort on any file-system error it encounters when
               reading from the file it is to send.  It can only send files with
               variable or fixed length record formats, therefore,  Wylbur  Edit
               or Packed format files will cause an error.

       "BLKSIZE not a multiple of LRECL for RECFM=F"
               KERMIT-TSO  will  refuse RECEIVE request and return to the KERMIT
               prompt.  The BLOCKSIZE is not an integral multiple of  the  LRECL
               when RECFM F (fixed) is specified.

       "LRECL not less than BLKSIZE-4 for RECFM=V'
               KERMIT-TSO  will  refuse RECEIVE request and return to the KERMIT
               prompt.  The LRECL for RECFM=V (variable) must be four less  than

                                      -7-
107/10/84                                                             KERMIT-TSO



               the BLKSIZE to include the block descriptor work (BDW).

       "Open for dataset failed"
               Indicates a problem opening the dataset.

 5. Reference

 For  a more detailed explanation of Kermit or information regarding the IBM-PC,
 consult the Kermit manual, Kermit Users Guide and Specification.  The manual is
 available in the Reference Library at USITE.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

                                      -8-