*****************************************************************
*                                                               *
* ASMGEN.COM - by J. Gersbach   and  J. Damke    (Ver. 2.01)    *
*                                                               *
* A program to generate cross-referenced assembly language code *
* from any executable file.                                     *
*                                                               *
*****************************************************************



*  PREFACE  *


This program will generate 8086/87/88 assembly code text
that is compatible with the IBM Personal Computer Macro
Assembler from any executable diskette file up to 65,535
bytes.  The output can be routed to the console or a disk-
ette file.  A reference list may be generated separately or
embedded at the appropiate instruction counter address in
the assembly code.

Some manual touch up will be required before reassembly, but
nearly all the typing is done for you by ASMGEN and anything
questionable is marked with "??".

A file of sequential instructions may be resident on the
same diskette to indicat to ASMGEN which addresses contain
code, byted, words, or strings.  This file may also include
instructions to assume segment register values or toggle the
output of assembley code text, generation of the reference
table, 8087 mnemonics, of the inclusion of embedded reference
information in the assembly file.

DEBUG may be used to browse through the executable file to
determine the starting locations of code and data to develop
the sequential instruction file.  It is important to accu-
rately specify these locations for an accurate reference
tabel and minimum touching up of the ASM output text.

The number of references within the file determines the amount
of memory required since a reference tabel is built in
memory during the first pass.  Disassembly is done from disk
and only one file sector is in memory at any given time.
Therefore memory size does not limit the size of the file
to be disassembled.  48K bytes of memory will be enough for
most programs but a few will need 64K or 128K.  One diskette
drive is sufficient but two is more convenient.


*  STARTING ASMGEN  *

There are two ways to work with ASMGEN:  either by using the
command menu or by calling ASMGEN with parameters.
Following are the descriptions of both options.

*  USING THE ASMGEN MENU  *

The program is invoked by typing:  ASMGEN

You are then prompted for a file specification.  Respond with
the name of the executable file from which you wish to
generate the assembly code.  The executable file will normally
have an extension of .EXE or .COM.  ASMGEN will check this
file spec for validity and then respond with a prompt that
includes a summary of the command letters indicating that
you may give it a command.  The executable file contents
are not checked for valid code and ASMGEN will try to dis-
assemble text or compressed BASIC files and produce unintell-
igible assembly code.

The commands are:

X filespec      This file spec replaces any previous executable
                file spec.  The usual file extension is .COM
                or .EXE

                EXAMPLE:  X DATE.COM


A <filespec>    The executable file is disassembled and the 
                assembly code is routed to the specified file.  
                The usual file extension is .ASM. If the filespec 
                is omitted, the output will default to the 
                console.

                EXAMPLE:  A DATE.ASM

R <filespec>    The reference table is sent to the file 
                specified. The usual file extension is .TBL.  If 
                the filespec is omitted, the output will default 
                to the console.

                EXAMPLE:  R DATE.TBL

Q               The program is terminated and control returned to
                DOS.


Each time a command has been executed, ASMGEN waits with a one 
line prompt for the next command.

X <filespec>, A <CON>, R <CON> or Q ?

The default filespec for each command is shown in brackets.  
Enter the next command of your choice as described above.


*  USING ASMGEN WITH PARAMETER CALLS  *

Up to three file specifications may be included when ASMGEN is 
first called from DOS.  The executable file's name is given 
first, followed by specifications for the assembly and reference 
table files.

EXAMPLE:  ASMGEN DATE.COM, DATE.ASM, DATE.TBL

If a semicolon follows the last filespec, ASMGEN will exit to DOS 
when the command has been executed.  If no semicolon is entered, 
ASMGEN will display the menu options described above and wait for 
further input after executing the command.

EXAMPLE:  ASMGEN DATE.COM, DATE.ASM;

If the filespec for the .ASM file and/or .TBL file is omitted,
ASMGEN will generate first the .ASM file, then a .TBL file using
the filename of the first filespec.

EXAMPLE:  ASMGEN DATE.COM,,; creates DATE.ASM and DATE.TBL and 
                             exits to DOS.

If only the reference table is desired, the dummy name NUL should 
be entered in place of an .ASM filespec

EXAMPLE:  ASMGEN DATE.COM, NUL, DATE.TBL

If only one filespec is given when the program is called, the 
reference table is built in memory and then the menu options are 
displayed for further commands.

EXAMPLE:  ASMGEN DATE.COM


*  PROGRAM EXECUTION  *

The disassembly is done in two passes through the scource file.  
On pass #1, the reference table is built in memory and the actual 
output is generated during pass #2.  Once the reference table is 
established, it remains in memory until an X or Q command is 
issued, and subsequent A and R command executions skip pass #1.  
This saves a lot of time when the executable file is large.

Three contiguous data areas are built dynamically in memory 
during pass #1. First is the compressed sequential instruction 
list.  Second is a list of pointers for .EXE files that point to 
the locations of all relocatable variables in the program, also 
arranged in numerical order.  These are established before 
reading any code.  Third, the reference table is then built in a 
higher area of memory as pass #1 progresses.

If all available memory in the program segment is filled before 
the first two data areas are completed, ASMGEN will abort to the 
command prompt. After the reference table is started, a shortage 
of memory will produce the message "Reference Table Incomplete 
Due to Insufficient Memory" and continue.

Ctrl-Break may be used at any time to interrupt a command in 
progress.


*  READING THE ASSEMBLY CODE FILE (.ASM)  *

This file begins with a title taken from the executable file's 
name and date followed by the current date (in brackets).

If not inhibited by the  M  switch in a SEQ file (explained 
later), the macro library will appear next in the file.

Next will be a .RADIX 16 pseudo-op which tells the macro 
assembler that all numbers are in hexadecimal form.

Then comes a header that indicates a starting value for the code 
segment, stack segment, instruction pointer and the stack 
pointer.  The stack pointer is usually set to FFFF for .COM files 
but may be somewhat less depending on available memory.  These 
values are passed by the linker for .EXE files.

The first ASSUME statement might come next.  There is one 
generated for each segment that begins with code.  All segment 
registers are designated according to the current set of ASSUMEs.  
They will sometimes be incorrect, so all ASSUME statements should 
be checked prior to re-assembly.

The disassembled output follows, terminated by an END statement 
and the execution address.  An ORG psuedo-op is included if 
required.

The text is compatible with the IBM Macro Assembler and the 
format is the same except for RETurns.  To avoid the need for 
PROCedure titles, special mnemonics are provided for all RET 
instructions.  These are defined in the macro library at the 
beginning of the file.  Only macros that are needed for the 
current file are produced.  The optional embedded commands that 
make up the reference table enhance the readability of the file.  
For very large files, this is sometimes undesirable and a 
separate reference table is best.

When invalid instructions are encountered in code areas, they are 
reproduced as byte values followed by "??".  If a near jump is 
defined previously in the code, and it is within range of a short 
jump, a NOP instruction is inserted after the jump.  The 
executable file created with this .ASM file and the Macro 
Assembler and Linker will then be the same length as the original 
file. This makes it less important to differentiate between 
labels and numeric constants since the label values and their 
offsets within the file will be the same.  The fundamental 
problem of disassembly is in knowing if the original assembly 
code defined a number as a label which changes as a function of 
it's position or as a number that always remains the same.  If 
you make changes in the assembly code however, you must properly 
specify all values. You might as well remove all NOPs at the same 
time.

Labels are five characters long and begin with "L".  Segment 
labels begin with "S".  The remaining characters are the current 
instruction counter in hex form, thus making each label unique 
and showing it's location in the original file.  The instruction 
counter is continuous throughout the assembly code without 
resetting at segment boundaries.  The segment labels are then in 
byte as opposed to paragraph form.  In those cases where a label 
value is modified by an ASSUME statement, the original value is 
included as a comment in the referencing instruction so that it 
may be easily changed back if it was not intended as a location.

The word "Relocatable" is printed at the end of any line that 
contains an ablolute paragraph value.  These are values that DOS 
modifies after loading but before executing a program.  They are 
used for loading segment registers that are sensitive to the 
program location in menory.  Relocatable values are not modified 
by ASSUMEs.  ASMGEN converts these numbers from paragraph to byte 
values by multiplying them by sixteen so that they will fit 
within the 16-bit instruction counter field.  When the paragraph 
value is negative or exceeds 0FFFH, it is left unchanged and a 
warning (??) is issued on that line.  When a program larger than 
64K bytes is being disassembled, it should be divided into 
smaller files.

All words are produced as labels, except when the "L" switch has 
been enacted in the .SEQ file (explained later).  The label name 
indicates it's numeric value and, if it does not occur on an 
instruction boundary, the name indicates it's position relative 
to the current instruction pointer is given by an EQU statement.  
Therefore the Macro Assember will assume that it is a location, 
but it is easily changed to a constant since the value is given 
in the label name.  The word OFFSET precedes a label whenever it 
is questionable whether it is a label or an immediate value.  You 
must decide which of the labels should be constants and which of 
the constants should be labels, and change them accordingly.  
When changing labels to numbers, be sure to append an "H" if the 
number ends with a "D" or a "B" since the Macro Assembler will 
otherwise assume that it is decimal or binary.

Bytes are always treated as constants.  An optional switch may be 
included in the .SEQ file (explained later) which enables numbers 
instead of labels if all references to the value are data segment 
and immediate operation types.

An effective procedure to follow in attempting to understand the 
assembly code file is to look first for the message text area, 
the input commands, and the simpler subroutines.  Then add label 
names to addresses in the .SEQ file (explained later) that 
remind you of their purpose.  Add comments to the labels.  If 
these names are well chosen, the larger routines eventually will 
become clear.  The embedded references are produced as labels so 
they will retain their meanings as they are changed.

It is also helpful to spend some time studying the structure of 
data areas. Vector tables, which are frequently used to control 
the program's flow, reveal the program's structure very quickly.  
If some routines do not have labels at the beginning, it is 
usually because the code or tables that reference them (or the 
segment register assumptions) are not properly defined in the 
 .SEQ file.


*  READING THE REFERENCE TABLE (.TBL)  *

A referencee is defined as a number that is referenced somewhere 
in the program.  It may be a program loaction or a numeric 
constant.

A referencor is is defined as the address in the program from 
which a reference is made to the referencee.

Each entry is composed of a referencEE  followed by a list of 
referencors.  If more than one line is needed, additional lines 
are indented to the first referencor position.  The referencEE is 
followed by an "S" if it includes references to the beginning of 
segment.  The referencor is followed by two letters, the first of 
which represents the segment register that is implied or prefixed 
in the referencing instruction.  The second letter indicates the 
type of operation on the referencEE.  When the reference entries 
are embedded in the assembly code, all values are preceded with 
the letter "L".

-----------------------------------------------------------------
1st letter      |  2nd letter
SEG REGISTER    |  TYPE OF OPERATION
-----------------------------------------------------------------
C  code         |  J  jump         M  modify - INC, ADD, etc.
S  stack        |  C  call         I  immediate - value or offset
D  data         |  R  read         T  test or compare
E  extra        |  W  write        ?  unknown or ESC instruction
                |  P  port
----------------|------------------------------------------------



*  WRITING/READING THE SEQUENTIAL INSTRUCTION FILE (.SEQ)  *

The sequential instruction file is a list of special instructions 
to ASMGEN which the user creates.  The file takes the form of a 
list of hexadecimal addresses and single-letter instructions or 
generation switches.  If used, the .SEQ file must be on the same 
diskette as the source file and have the same name as the source 
file with an extension of .SEQ.  Each instruction in the file 
must be in one of the following formats:

addr    command
or
addr    command         ;comment
or
addr    command         label   comment
or
addr    command         label   comment ;comment

"addr" represents the instruction pointer value.  All addr values 
must be in numerical sequence in the file.

"command" may be either a toggle switch or a generation 
instruction.

"label" is optional and replaces the label generated for this 
address with this non-blank string.

"comment" is optional and must be preceded by "label" unless the 
dummy label "." is used.  Everything following "label" is treated 
as an address comment and will be printed in the ASM file behind 
the generated instruction.  The address comment may be up to 255 
characters in length and should not contain a semi-colon.

";comment" is optional.  Anything following a semi-colon in the 
 .SEQ file instructions is considered as a comment in the .SEQ 
file only and is not added to the generated .ASM file.

"label" and "comment" are not allowed when a generation switch is 
coded, but a ";comment" may be used to help clarify the .SEQ 
file.

The .SEQ file is read into memory before the first pass starts.  
The addresses and commands will be compressed, but "label" and 
"comment" will be held in memory one to one.  An effect of this 
is that memory space required for dis-assembly increases with 
each "label" and "comment" added to the .SEQ file.


*  DESCRIPTION OF GENERATION SWITCHES  *

THE VARIOUS TOGGLE SWITCHES ARE SET TO ON BY DEFAULT.  Switches 
may be toggled on and off at any point in the .SEQ 
file/disassembly.

All options switches except /M and /H can be either toggled or 
directly set by the user.  A suffix of "+" turns the switch ON, 
and a suffix of "-" turns the switch OFF.  Switches encountered 
in the file that have neither of these suffixes are toggled to 
the opposite of their state at the time; ON switches are turned 
OFF and OFF switches are turned ON.

/B - generate byte references

When ON, byte and word references are included in the reference 
table.  When OFF, only word references are generated.

/E - embedded references in ASM file

When ON, reference table entries are inserted in the text just 
before the referencee's definition statement.  When OFF, these 
entries are not included with the disassembled text.  The entire 
reference table can be printed with the "R" command.

/F - 8087 mnemonics

When ON, ESC instructions are produced.  When OFF, ESC 
instructions are assumed to be 8087 instructions and 8087 
mnemonics are produced.

/H - append hex "H"

When this switch appears at any point in the .SEQ file, an "H" is 
appended to all hex numbers.  This does not, of course, apply to 
the labels which are hex values preceded by the letter "L".  The 
 .RADIX 16 pseudo-op is omitted which allows the assembler's radix 
to default to decimal.  This switch defaults to NO H APPEND.  
Note that it will be set only once.  It retains it's value until 
the next .SEQ file is read.

/L - generate label or number

When ON, all word references are treated as labels.  When OFF, a 
word reference is treated as a constant if all referencors are 
data immediate types.

/M - suppress macro library

When this switch appears at any point in the .SEQ file, no macro 
library is included in the text output.  The DEFAULT IS THAT THE 
MACRO LIBRARY WILL BE INCLUDED.  Note that this switch will be 
set only once.  It retains it's value until the next .SEQ file is 
read.

/O - control ASM output

When ON, ASMGEN will output the generated text.  When OFF, output 
will be suppressed.

/R - control TBL output

When ON, ASMGEN will output the generated reference data.  When 
OFF, the reference table is not printed.

/T - control trace output

When ON, up to 16 bytes of object code are included as comments 
in each line of the assembly code file.  When OFF, object code is 
not included.


*  DESCRIPTION OF .SEQ FILE COMMANDS  *

A - assume

The following lines contain ASSUMptions for segment register 
values.  They become effective at the address specified by this 
instruction and may be modified anywhere in the disassembly. The 
required format for assumptions is:

& 0400  DS

The ampersand indicates a continuation of the A instruction.

In this example, a data segment beginning at a instruction 
pointer value of 400 will be assumed until another  A  
instruction changes it.  CS, ES, and SS are also supported.  The 
segment assumptions are used for effective address calculations 
only.  The code segment assumption does not affect the 
instruction pointer value.

B - bytes

The bytes encountered in the source file are assumed to have 
meaning as single byte values.

C - code

The bytes encountered in the source file are assumed to be valid 
8088 machine language instructions.

D - generate data operand

The operand of the instructions is changed to immediate data.  
Subsequent bytes are interpreted as "C" (code follows).

I - initial value for IP

The hexadecimal value on this line overrides the instruction 
pointer value at the beginning of the file - not to be confused 
with the address at which execution begins.  The default values 
are 0000 for EXE files and 0100H for COM and other files.  The 
execution address following the END statement is omitted if this 
option is invoked.

S - strings

The bytes encountered in the source file are assumed to form 
text.  Quoted text is produced for valid ASCII characters and 
byte values for others.

# - defined length strings

The first byte encountered in the source file contains the length 
of the character string which begins with the next encountered 
character.  This length value may be overridden by a subsequent 
SEQ file instruction.

$ - defined length strings

The first byte encountered in the source file contains the length 
of the character string which begins with the next encountered 
character plus the length byte itself.  This length value may be 
overridden by a subsequent SEQ file instruction.

W - words

Pairs of bytes encountered in the source file are assumed to have 
meaning as word values.

X - repeating data structure

A cyclic data structure is assumed to begin at the specified 
instruction pointer value.  The structure definition may follow 
and is prefixed by an ampersand (&) to indicate the continuation 
of this instruction.  If the definition does not follow, then the 
most recent definition is used.  If no structure is yet defined, 
then an error message is displayed.

The following elements may be used to define the structure:

& NNNN S  -  The next NNNN bytes are defined as string characters
& NNNN B  -  The next NNNN bytes are defined as byte values
& NNNN W  -  The next NNNN bytes are defined as word values
& XXNN $  -  The next sequence of bytes is defined as NN fields.  
             Each field consists of a length byte and a string of 
             characters. The length of each field is contained in 
             the first encountered byte. The high nibble (XX), if 
             non-zero, is a bit mask of the length field within 
             the byte. The length field is right-justified within 
             the byte after the byte value is sent to the output
             file.



*  EXAMPLES OF .SEQ COMMANDS  *

This example .SEQ file shows all the possible instructions in the 
appropriate format.

;All switches are on at the beginning.
0       /T      ;no object code as comments in output
0       /M      ;no macro library in output
0       /H      ;append "H" to all numbers
00H     /A      ;assume the following segment values
;Note that the ampersand (&) indicates the extended ASSUME
& 380   DS      ;the data segment starts at 380 hex
& 380   ES      ;the extra segment starts at 380 hex
0200     I      ;initialize the instruction pointer to 200
0200    /F      ;introduce 8087 mnemonics (not ESC)
0200    /E      ;no embedded references
0200     C      ;code begins at 200
0203H    W      ;words are at 203
0207     C      ;more code starting here
220      X      ;complex data structure begins here
& 3      W      ;words
& 1      B      ;byte
& 0E02   $      ;2 strings starting with the 2nd byte follow
                ;bits 3,2,1 of the first byte contain the length
                ;of the string including the length byte.
                ;the high nibble (0E) is the mask.
                ;see also # in summary below
& 1      B      ;byte
                ;the structure repeats until 351
351      B      ;bytes
358      C      ;more code
380      S      ;strings - list of messages
421      W      ;words
4FD     /B      ;no further byte references
502     /R      ;garbage here - turn off reference generation
502     /O      ;and output
600H    /O+     ;valid code - turn output back on
600     /R
600      C
1A60    /O-     ;output file about to fill diskette - turn output
                ;off but keep scanning for references. another
                ;run will be needed to get the remaining code.
1B00    /D      ;treat operand as immediate data
1DFD    /B+     ;continue with byte references
1F45     W      user_prt        ;user provided labels will
2256     S      $MSG            ;translate to upper case


Comments may be included if preceded by a semicolon.

Alphabetic characters may be either upper or lower case.

An "H" may follow the hex address.



*  SAMPLE SESSION  *

The external command CHKDSK.COM will serve as an example for this 
sample session because it is short.  The .SEQ file is also short 
and easy to generate. Only these few instructions are needed.


0100  /T  ;include object code as comments in .ASM file
0100  /E  ;simpler output without references
04F7H  S  ;messages
04F7H /H  ;append "H" to numeric values

Using DEBUG, browse through CHKDSK.COM to see how this was 
arrived at. Usually, but not always, the best procedure is to 
assume code.  If the code appears unintelligible, display it in 
hex/ASCII.  If it is not text, assume bytes.  Label positions in 
the first disassembly may indicate that some locations should be 
words.  Next, generate the .ASM file by typing

ASMGEN CHKDSK.COM <enter>
A                 <enter>

The assembly code can be viewed on the screen.  Then type

A CHKDSK.ASM      <enter>

to save the assembly source code to a file.  Then,

R CHKDSK.TBL      <enter>

to save the cross-reference table to disk.

The Macro Assembler, Link.exe and Exe2bin could now be used to 
assemble CHKDSK.ASM, link it to .EXE and convert it to a .COM 
file.  No modification should be necessary in this case.

If working with code that is to be modified, the symbol types 
must be correctly specified as locations or as constants.  If 
they are constants, place them outside of any segment.  The label 
names may then be changed to make the code more readable.


EndOfFile