OPA - A PRIVILEGED TASK TO DISPLAY A SNAPSHOT MAP OF THE CURRENT CONTENTS
	OF POOL!!!! (for RSX-11MPlus V.1)

	AS MODIFIED FOR MPLUS with accounting - Kitty Bethe

NOTE WELL:  This program is sufficiently valuable to all system managers/
programmers who have pool space problems that it is (to my mind) well worth
the risk of using.  However, it is necessary while this program is 
scanning through pool to be on the system stack.  It catches
its own odd address or memory protect traps, and reports them 
rather than causing a system crash.  The biggest problem
from overuse is that some device drivers may require frequent access to
system state (i.e. forking) in order not to lose interrupts.  While this
task is collecting data, the EXEC cannot handle fork requests.  It does,
however, seem to work well on our 11/70 system, and has given us a
good deal of insight into what fragments and/or gobbles up pool.

The program output will appear on the invoking terminal; however LOG can
be used to run it in order to get a copy on disk (LOG OPA.LOG/TI=TI: or
in version 2 use LGG instaed of LOG)

If the task gets a command-line switch of /F, then it will list the free-
segment list described below, after the task accounting output and before
the map output.

Output format:

	The output is in 3 parts:
		- active task pool usage summary
		- free segment list (optional)
		- visual map of pool

	An example of output from our system is at the end of this document,
a more complex one can be found in OPA.LOG in this UIC. A description of each
part of the output follows.

	Active task pool usage summary

Each active task is listed along with its header size (0 if checkpointed
or if it has an external header),
the number of open files it has (window blocks), the number of outstanding
QIOs, the number of receive (data or by ref) packets queued to it, the
number of clock queue entries, the number of attachments it has ( one for
each library, common, dynamic common, and one to itself if it is fixed),
the number of other miscellaneous bytes charged to it are from specified
asts, ast completions, parent/offspring blocks (charged to offspring),
file control blocks (which have overflowed from the ACPs internal buffer)
and pcb vectors (these could be separated out in a future version). The
total bytes a task is using in pool include its PCB and TCB as well as
the previous items. Note that all numbers are decimal and the sizes for
the data structures are included in the header line.

	Free segment List

1st line: # of fragments of pool
2nd line: total words of pool
3rd line: largest fragment
4th line: total free words

the above 4 lines are always printed whether or not /F was used

next n lines: addresses and sizes of all free segments in pool
next line: total # words free in pool

	Visual Map of Pool

In this display, each ASCII character represents a minimum allocatable piece
of pool, i.e. 4 bytes.  Each line is 64(10) characters, corresponding to
400(8) bytes of pool.

Free area is shown by --------

Used but not identified is shown by ????????

The following structures are grouped alphabetically within delimeter class:


@	is a common PCB vector for an installed task

[ASn]	is a specifed-ast control block, where n is the ast type code.
[...]	is some other ast control block (completion ast)
[BIO..TT:]  is the ast control block for terminal buffered I/O
[CT]	is a common task image PCB
[CQn]	is a clock queue control block, where n is the type (see system data
	structure definitions for types)
[FDX..TT:]  is an ast control block from the full duplex tt driver
[W]	the primary pool portion of a window block for a file
[+taskname+]
	a receive by reference queue packet for the task "taskname"
[*taskname*]
	a receive data packet (primary pool portion) for "taskname"

*A*	represents an attachment discriptor block
*U*	represents a UMR allocation block
*W*	represents a wait for UMR allocation block
*x*	is a logical assignment control block, where x is the type (global
	asn is type 0).  The most interesting from the point 
	of pool fragmentation is */* which is a login assignment,
	which of course will not move while the terminal is logged in.

!M	is a mount control block

^taskname
	is an offspring control block where the parent task is taskname.

(_FCSRES)
	is a PCB for a permanent partition, while (>...OPA) is a subpartition
	control block for an active task, (=F11ACP) is a fixed task. A
	subpartition control block for a driver is (  ZB:  ), while (!F4PFSL)
	is a dynamic or PLAS region, and (+...EDI) is the read only part of
	a multi-user task. Non-memory resident installed commons and libraries
	have PCBs also, these are marked as ($FCSRES) - checkpointed tasks
	have PCBs also, these are marked as (-HRC...).

<CP>	is a checkpoint file control block
<DCB+UCB+SCB=DV:##> 
	The data structures for a loadable driver with a loadable
	database.  It will not handle data structures
	which have oddball SCB lengths for some reason.
<FCB DBn:> 
	a file control block found for the index file on DBn:
<HEADER ...OPA###########> 
	is of course a task header for task ...OPA. Note that this is one 
	of the significant pool fragmenters, particularly if you get either 
	MCR or an ACP checkpointed, since the header then will wind up in the 
	middle of pool somewhere when the task comes back in, and since the
	task never exits (just stops) the header never goes back out.
<IN TTnn:>
	is an I/O packet waiting for input from TTnn:
<IO DVn: > 
	is an I/O packet either currently in use or queued to device DVn:
<OU TTnn:>
	is an I/O packet waiting for output to finish on TTnn:
<PAKT OPT>
	is a saved I/O size packet for QIO optimization.  These devils will
	really fragment your pool, as they get allocated mostly when your
	system is busy, then hang around later so it's hard to move/get 
	rid of them, except of course by turning off the optimization.
<///TCB FOR: ...MCR> 
	is the task control block for task ...MCR, e.g.
<VCB...DBn: > 
	the volume control block for device DBn:


Note that in general the stuff at the top of pool is put there by VMR, which
incidentally from this program I learned does a terrible job by not filling
any holes created by removing tasks, for example.

Comments and suggestion are welcome, but please don't complain if your system
crashes.  Hopefully I or others will get around to doing a few more data
structures,and there will be fewer areas labelled ????????.  Keep in mind
that it will never be possible to do all areas, since privileged tasks and
drivers may take blocks out of pool which are not referred to by any standard
data structures.  Also some structures are pointed to only by things in
the task headers, and if the task is checkpointed there is no way to find
them.  A good example is window blocks for files opened by various active
tasks.

ORIGINAL AUTHOR:		MPLUS version with task accounting:
	Jim Neeland			Kitty Bethe
	Hughes Research Labs		Bankers Trust Company
	3011 Malibu Canyon Rd.		130 Liberty St.  37th floor
	Malibu, California 90265	New York, N.Y.  10006
	(213) 456-6411 ext. 333		(212) 775-4190


AN EXAMPLE OF OPA DONE VIA LOG:




		ANALYSIS OF ACTIVE TASK POOL USAGE:

                |---------- COUNTS ----------|
  TASK  HEADER   OPEN        RECV        ATTCH
  NAME   SIZE   FILES  QIOS* PKTS   CLQ  MENTS  OTHER   TOTAL
       (BYTES)    (8)  (40)  (40)   (16)  (12) (BYTES) (BYTES)

******       0     3     0     1     1     1      56       252
...LDR     102     0     0     0     0     1       0       218
MCR...     114     0     0     0     0     1       0       230
F11ACP     138     0     0     0     0     1       0       254
COT...     126     1     0     0     0     1       8       258
HRC...     138     0     0     0     0     1       8       262
BAP0       126     0     0     0     0     1      36       278
VT2        102     0     0     0     0     1      28       246
QMG...     134     1     0     0     1     2       4       290
TTP5       126     0     0     0     0     1      44       286
AT.V2      150     0     0     0     0     2      32       310
LOGT33     114     1     0     0     0     1       8       246
ED2T34     154     3     1     0     0     3       6       364
TT6        174     0     0     0     0     3      24       338
______________________________________________________________

TOTALS    1698     9     1     1     2    20     254      2480


     * THIS ANALYSIS WILL NOT FIND MOST QIOS TO DMC LINES
****** (ANALYSIS FOR INACTIVE TASKS - OPEN FILES ARE INDEX FILES)

NUMBER OF INSTALLED INACTIVE TASKS:     45
  BYTES USED FOR THEIR TCBS:   3060


POOL MAP: . . . . . . . * . . . . . . . * . . . . . . . * . . . . . . .
034400:                                                              @@[
035000: CT]*A*(=F11ACP)<TCB FOR: F11ACP>(_FCPPAR)(_SHFPAR)(_TKNPAR)(_DCL
035400: PAR)(_MCRPAR)(_SYSPAR)( TT:   )[CT](!TTCOM )( XM:   )( NL:   )( 
036000: VT:   )( RD:   )( CO:   )( MM:   )( DB:   )(_DRVPAR)*A*(=...LDR)
036400: <HEADER ...LDR###########><TCB FOR: ...LDR>(_LDRPAR)(_SECPOL)*0*
037000: *A*[CQ0](>ED2T34)-@[CT]!M!W@@-[+QUEMGR+]!M!W@<IN TT34:><TCB FOR:
037400:  ...RMD>!W*1*!W!M!W*1*!W*A*-*A*@@*0*!M<HEADER MCR...############
040000: ##><VCB...DB4: ><FCB DB4: >(>MCR...)<TCB FOR: ED2T34><VCB...DB0:
040400:  >*A*-*/*@[AS5][AS2][AS2]!W<PAKT OPT><PAKT OPT>*0**0**0**0**A**A
041000: **A*(>COT...)!W!W(>HRC...)<HEADER HRC...####################>*A*
041400: [AS5]???????[AS2]*0**0**0*<CP>*0**A*($F4PRES)[CT]@[CT]-<HEADER C
042000: OT...#################><TCB FOR: TIME  >(!F4PFSL)[CT][CQ2]($FCSR
042400: ES)*A*<DCB+UCB = VT1: %>*/**/*(>TTP5  )(>QMG...)<HEADER QMG...##
043000: #################><TCB FOR: TTP5  >??????*A*<TCB FOR: BAP0  >*/*
043400: ^QMG...<HEADER TTP5  #################>^QMG...<FCB DB0: >(>LOGT3
044000: 3)*1**A**1*-(>BAP0  )<HEADER BAP0  #################><TCB FOR: L
044400: OGT33>[AS5]*A**A*<TCB FOR: ...CMP><TCB FOR: ...EDI>(+...EDI)<PAK
045000: T OPT>*/*[CT]-*/*<TCB FOR: ...TCR><HEADER ED2T34################
045400: ########>^LOGT33--[CT]-*1**1*----<TCB FOR: TTP4  >(!SCRPAR)*0*--
046000: */*--<PAKT OPT>*0**0**0**0**0**0**0**0**0*--<VCB...DB2: ><TCB FO
046400: R: ...ED2>[CT]*0*(+...ED2)*0*--<FCB DB2: ><TCB FOR: ...LOG><TCB 
047000: FOR: QUEINI>*A*-*0**0**0**0**0**0**0**0**0**0**0**0**0**0**0**0*
047400: *0**0**0**0**0**0**0**0**0**0**0**0**0**0**0**0**0**0**0**0**0*<
050000: DCB+UCB = VT2: %>(>AT.V2 )-----[EF]---(!QUEPAR)<HEADER LOGT33###
050400: ###########>^AT.V2 -------[AS1]--<TCB FOR: RSTQUE><TCB FOR: QUEM
051000: GR><TCB FOR: ...QUE><TCB FOR: VT2   >----<TCB FOR: AT.V2 >(>VT2 
051400:   )--------<TCB FOR: TT6   >*A*<HEADER VT2   ###########>-------
052000: (>TT6   )[AS3][AS2]*A*-<PAKT OPT><HEADER TT6   #################
052400: ############>---(!OD1300)*A*<HEADER AT.V2 ######################
053000: #>---<TCB FOR: ...SRT><TCB FOR: BELL  >----*1*------------------
053400: ----------------------------------------------------------------
054000: <TCB FOR: COMREP>--------------------------[CT]-----------------
054400: ---------------------<TCB FOR: ...F4P><TCB FOR: ...TKB>---------
055000: <PAKT OPT>(!LINPAR)---------------------------------------------
055400: ----------------------------------------------------------------
056000: ----------------------------------------------------------------

			(ABOVE REPEATED MANY TIMES)

112400: ----------------------------------------<TCB FOR: PRT...><TCB FO
113000: R: ...SRD>-----------------<TCB FOR: ...PIP>@<TCB FOR: ...DMP><T
113400: CB FOR: QMG...>@<TCB FOR: SHF...>-----------------<TCB FOR: PMD.
114000: ..>@<TCB FOR: ...CA.>@<TCB FOR: TKTN  ><TCB FOR: ...MCR><TCB FOR
114400: : ...SAV><TCB FOR: MTAACP><TCB FOR: ...MOU><TCB FOR: MCR...><TCB
115000:  FOR: ...INS>@<TCB FOR: ...INI><TCB FOR: ...AT.>@<TCB FOR: HRC..
115400: .><TCB FOR: ...HEL><TCB FOR: FXR...><TCB FOR: F11MSG><TCB FOR: E
116000: RRLOG><TCB FOR: ...ERF><TCB FOR: ...DMO><TCB FOR: DCL...><TCB FO
116400: R: ...DCL><TCB FOR: COT...><TCB FOR: ...CON><TCB FOR: ...BYE><TC
117000: B FOR: ...BRO><TCB FOR: ...BOO><TCB FOR: ...ACS>(!FCSFSL)(!DEVCO
117400: M)(_IO PAR)(_GEN   )(_AMTBUF)<HEADER F11ACP####################>
AT.>^Z
>@ <EOF>