VT125 HGRAPH



        
        
       General Information
       -------------------
        
        


            In the VT125 version of HGRAPH the VT125 screen is  defined  to

       have  the  same number of pixels per nominal inch as the Visual 550.

       A consequence of this is that the size of the VT125 plotting page is

       reduced  to  10.2  by  6.3 nominal inches.  These are the dimensions

       that should be used when calling INIPLT if it is desired to  utilize

       the entire screen.  



            The code that drives the VT125 is a slightly modified  copy  of

       the 550 code.  Thus the logical unit number of the VT125 is the same

       as the logical unit number of  the  550  (logical  unit  number  7).

       Additional modifications not documented here will have to be made to

       create an HGRAPH library that supports both the VT125 and the 550.



            Since HGRAPH was designed to work with a  variety  of  physical

       plotting  devices,  its  subprogram  modules are divided into device

       dependent modules and device independent modules.  It should only be

       necessary  to modify the device dependent routines to provide HGRAPH

       support for the VT125.



            Additional modifications may be necessary  when using an  older

       model  DM/PL  single  pen   HIPLOT  plotter.    All  the  executable 

       statements in subroutine COLOR should be removed,  and all P, E, and

       F  commands contained in plotter messages in the  INIPLT and  ENDPLT

      routines should be removed.  The command 'UH @' is recommended as the

      command to be sent to the plotter in subroutine ENDPLT.





                                 VT125 HGRAPH                        PAGE 2



            The Visual 550  and  VT125  also  appear  to  have  differences

       regarding  the  ability  to  independently display text and graphics

       planes.  The VT125 seems to always display both text  and  graphics.

       If  this is undesirable, it is possible to control this to a certain

       extent from inside the program using the modified  HGRAPH  routines.

       Subroutine  erase  will  clear the graphics plane.  Subroutine plton

       will, in addition to entering graphics mode, clear the  text  plane.

       If  it  is  desireable  to  clear the text screen and remain in text

       mode, this can be accomplished by calling plton followed immediately

       by  calling  pltoff.   The file CLEAR.DAT has been provided to clear

       the graphics screen from outside the control  of  the  program.   To

       clear the graphics screen simply enter TYPE CLEAR.DAT.



            A couple of problems commonly occur when using HGRAPH.  When  a

       program  is  linked  with the HGRAPH library it is common to see the

       linker error message LIBRARY LIST OVERFLOW INCREASE  SIZE  WITH  /P.

       The  run  time error message STACK OVERFLOW may also be encountered.

       The solution to these problems is to use the following commands when

       linking programs with HGRAPH:

                r link
                <.sav file name>/P:400./B:1400=<list of object file names>
                <CNTRL/C>
        
       If the errors persist, the values 400 and 1400 can be increased.
        





                                 VT125 HGRAPH                        PAGE 3



            Since the VT125 does not  recognize  graphics  commands  unless

       they  occur  between the two commands to enter and exit REGIS (plton

       and pltoff), and since these commands may be  used  to  control  the

       text  plane,  if calls to HGRAPH routines result in a lot of garbage

       characters being printed on the terminal it will be due to the  fact

       that plotting was disabled and not reenabled before calling plotting

       routines.



            The routines that implement cursor control,  character  reading

       routines,   and  interactive  legend  developing  routines  are  not

       supported.  Do not attempt to use these routines.  They will not  be

       included in the library built using this version of HGRAPH.



            An indirect command file is  provided  to  compile  the  HGRAPH

       source  and  build  the  library  HGRAPH.OBJ.   To create the HGRAPH

       object library enter the command @HGRAPH.BLD.




                                 VT125 HGRAPH                        PAGE 4



        
        
       Device Dependent Routine Modifications
       --------------------------------------
        
        
       CIRCLE :  The subroutine circle is implemented by ENCODEing a  REGIS

                    command  to  move  to  the  location  specified  by the

                    parameters IX and IY.  The y coordinate is adjusted  to

                    account  for  the difference in screen origin locations

                    between the two terminals.  A circle is then  drawn  by

                    ENCODEing  the  circle  radius  into  the  regis circle

                    command  and  sending  this  message.   Since  the  550

                    version  of  HGRAPH  used  routines  implemented in the

                    terminal itself to draw circles, it  was  necessary  to

                    use the REGIS circle drawing command also.  A result of

                    this is that circles drawn using the VT125  version  of

                    HGRAPH  will  be  of  lower  quality than circles drawn

                    using  the  550.   In  addition,  since  the   terminal

                    implements  the  actual circle drawing, circles will be

                    plotted without regard to defined  pages,  frames,  and

                    windows.






                                 VT125 HGRAPH                        PAGE 5



       ERASE :  Graphics mode characters to clear  the  VT125  screen  have

                    been substituted for 550 control characters.  S(E)



       INIPLT :  Iniplt was changed to call plton to enable graphics.  This

                    call   replaced   outputting  specific  550  characters

                    intended to cause  a  particular  type  of  entry  into

                    alphagraphics mode.



       PENDWN :  Modified to only save up/down status of  pen.   The  REGIS

                    equivalent of a pen position is determined by a command

                    that accompanies the graphics coordinates.  This status

                    is looked at to determine the proper type of command to

                    accompany the coordinates when a screen position change

                    is made.



       PENUP :  Modified to only save updown  status  of  pen.   See  notes

                    accompanying PENDWN.






                                 VT125 HGRAPH                        PAGE 6



       PLOT :  The modifications  to  suboutine  plot  represent  the  only

                    significant changes to the HGRAPH source where the code

                    was actually changed instead of  replaced  by  a  REGIS

                    equivalent.   The changes reflect the fact that the 550

                    interprets  graphics  coordinates   relative   to   the

                    particular  state  that  it  is currently in (ie vector

                    mode, point-plot mode, etc.).  Regis commands,  on  the

                    other  hand, contain a command character along with the

                    graphics coordinates that indicate what action is to be

                    taken  (ie draw a vector, plot a point, etc.).  Another

                    difference is that the origin  of  the  REGIS  plotting

                    page  is  at  the  upper left-hand corner while the 550

                    origin  is  in  the  lower  left-hand   corner.    Plot

                    calculates  the proper point in the same manner for the

                    VT125 as for the 550.  When the screen coordinates have

                    been calculated the y coordinate is subtracted from 479

                    to  account  for  the  difference  in   screen   origin

                    locations.  The coordinate values are then ENCODEd into

                    the proper type of REGIS message based on  the  up/down

                    status  of  the  pen  and  output to the terminal.  The

                    current screen  location  is  saved  as  a  550  screen

                    coordinate.   This routine should be the first place to

                    look for  correcting  bugs  in  the  VT125  version  of

                    HGRAPH.






                                 VT125 HGRAPH                        PAGE 7



       PLTOFF :  Pltoff was modified to output the REGIS  graphics  command

                    terminator  ESC\ to exit graphics mode.  When pltoff is

                    called the cursor is also  homed  and  lowered  to  the

                    bottom  line of the screen.  This is done in an attempt

                    to keep possible subsequent  program  generated  output

                    from immediately overwriting the plot.



       PLTON :  Plton was modified to output the start of a  REGIS  command

                    string   (ESC   P   p).   This  causes  any  subsequent

                    characters output to be interpreted as  REGIS  commands

                    until  the  graphics  string terminator is encountered.

                    Each time plton is called the text screen is cleared.



       WRTSTR :  The subroutine wrtstr  in  the  hgraph  flecs  source  was

                    replaced  with  the  contents  of  the file wrtst2.flx.

                    This subroutine generates its own characters instead of

                    using  terminal  generated  characters.  Including this

                    routine adds simplicity  to  the  modification  at  the

                    expense of a certain loss of character quality.






                                 VT125 HGRAPH                        PAGE 8



        
       Routines Not Requiring Modification.
       ------------------------------------
        
                    COLTYP
                    DEFWIN
                    DMPPLT
                    ENDPLT
                    MARKER
                    WRITCH
        
       Unsupported Routines
       --------------------
        
                    CONLGN
                    CURSON
                    DEFWIN
                    FNDCUR
                    GETSTR
                    PUTCUR
                    REDSTR