LDM 106

                               DOC #130-380-007-00










                                    SUPER-MAC
                                 REFERENCE GUIDE
                                   VERSION 54


     SUPER-MAC                                                            Page 2



     COPYRIGHT (C) 1975 


     DIGITAL EQUIPMENT CORPORATION 


     The  information  in  this document is subject to change without notice and
     should not be construed as a commitment by Digital  Equipment  Corporation.
     Digital Equipment Corporation assumes no responsibility for any errors that
     may appear in this manual.  

     The software described in this document is furnished to the purchaser under
     a license for use on a single computer system and can be copied  (with  in-
     clusion  of DIGITAL's copyright notice) only for use in such system, except
     as may otherwise be provided in writing by DIGITAL.  

     Digital  Equipment Corporation assumes no responsibility for the use or re-
     liability of its software on equipment that is not supplied by DIGITAL.  



     Since  the  appearance of SUPER-MAC in the public domain, numerous enhance-
     ments have been made which improve both the applicability  and  portability
     of  SUPER-MAC  source  code.  During this enhancement process, every effort
     has been made to maintain compatibility for  source  code  generated  under
     earlier versions of SUPER-MAC.  


     This manual documents SUPER-MAC VERSION 54.  



     ARTHUR P.  GAUGHAN, JR.  22-SEP-80 


     SUPER-MAC                                                            Page 3



                                 CONTENTS



     1.1  Introduction


     1.2  Assignment Statement

          LET, LETB


     1.3  Conditional Statements

     1.3.1

     Condition Execution Statements

               IF

               IFB

               AND

               ANDB

               OR

               ORB

               ELSE

               ON.ERROR

               ON.NOERROR

               LEAVE

               RESTART

               GOTO

               THEN

     1.3.2

     Loop Control Statements

               FOR

               REPEAT

               UNTIL



     SUPER-MAC                                                            Page 4



               UNTILB

               THRU

               WHILE

               WHILEB

               $$END

     1.4  Miscellaneous Statements

               BEGIN/END

               $CALL

               CALLG

               $RETURN

               POP, POPB

               PUSH, PUSHB

               JUMPTO

               CASE, CASEB

               PROCEDURE

               ENTRYPOINT

               PROBE, PROBEB

               BEGINMODULE


     1.5  Error Messages



     SUPER-MAC                                                            Page 5



     1.1  Introduction 

     SUPER-MAC  is  a set of structured programming macros that allows
     programs to be written in a high level, easily  understood  lang-
     uage.   It  is  assumed  that the user is familiar with macros in
     general and with MACRO-11 in particular.  

     The language statements and clauses within this guide are divided
     into three categories:  Assignment statement, Conditional  state-
     ments  and Miscellaneous statements.  The Conditional category of
     statements is further divided  into  Conditional  Execution  type
     statements and Loop Control statements.  

     There  are three branch type statements:  LEAVE, GOTO and JUMPTO.
     The LEAVE and GOTO statements are  cased  special  branches  used
     with the IF statement.  They are, therefore, included in the Con-
     ditional category.  The JUMPTO statement is included in the  Mis-
     cellaneous category.  

     As  a  general rule, most SUPER-MAC statements can be single-line
     statements  or  multiple-line  (nested)  block   statements.    A
     single-line  statement  must be completed on one source line;  no
     continuation lines are allowed.  Single-line statements should be
     as  short  and simple as possible.  Comments may also be included
     on a source line.  All the general rules, conditions, etc.,  that
     govern  MACRO-11 also govern SUPER-MAC.  Spacing on a source line
     is very important.  The elements should be separated by  a  comma
     or a space.  Tabs should never be used for spacing.  For example:
     The expression A+B is interpreted differently than A + B.  

     All  the  conditional  statements can be written as multiple-line
     nested blocks.  Each level of nesting within a block must be ter-
     minated  with an associated END statement.  Each level of nesting
     should be indented two spaces.  

     User  written macros or assembly language instructions may be in-
     cluded in a program if desired.  As a debugging aid, if the  sym-
     bol  LST$$ is defined, it will cause generated code and labels to
     be listed.  All labels and symbols generated  by  SUPER-MAC  will
     have  a "$" prefix.  Short branches are defaulted to generate op-
     timized code.  If the symbol LNG$$ is defined, it will cause long
     branches to be generated.  All programs must begin with the macro
     call SMACIT.  This call initializes SUPER-MAC and .MCALLs all  of
     the  SUPER-MAC  macros and any associated primitives.  This guide
     contains examples of all statements.  In nested  block  examples,
     the  END  statements  associated  with a particular statement are
     noted.  When an example includes assembly language  instructions,
     that  instance is pointed out.  A list of possible error codes is
     included as well as an assembled listing of  some  typical  exam-
     ples.  All legal PDP-11 source and destination operands are legal
     in SUPER-MAC.  





     SUPER-MAC                                                            Page 6



     1.2  Assignment Statement 

     LET  and  LETB  are  the  only assignment statements contained in
     SUPER-MAC.  

     LET(B) STATEMENT 

     The  LET(B)  statement is an arithmetic assignment or replacement
     statement.  

     The form of the statement is:  

               LET(B) [Destination] <assignment operator> expression 
                   [Operand   ] 

     expression is in the form:  

               (unary  operator)  operand (binary operator operand bi-
     nary operator...) 

     Where:  

               (     ) means optional 

                                   NOTE

     No  code  is  generated if the source operand is identical to the
     destination operand (single source operand only).  a  message  is
     printed if identical.  

     Example:  

             The statement 

                      LET -(R0) := -(R0) 

             will generate  ".PRINT ;NO CODE GENERATED" 

             not the desired   MOV -(R0),-(R0) 

     In order to get the desired result, the following construction is
     necessary:  

             LET R0 := R0 - #4       SUB #4,R0 

     Care  must  be  taken  in the construction of a LET(B) statement.
     Some constructions (where the destination operand  type  modifies
     the  register  used  on the formation of the destination address)
     appear to be what the programmer desired, but the assembler  will
     generate code that is different from the intent.  

     Example:  

          The statement 


     SUPER-MAC                                                            Page 7



               LET (R5)+ := R1 + R2 

          will              generate              the             code
     MOV R1,(R5)+ 
                              ADD R2,(R5)+ 

          not the desired     MOV R1,(R5) 
                              ADD R2,(R5)+ 

     In order to get the desired result, the following construction is
     necessary:  

     LET (R5) := R1           ;MOV R1,(R5) 
     LET (R5)+ := (R5)+ + R2  ;ADD R2,(R5)+ 

     SUPER-MAC  recognizes  all  the  special  characters  accepted by
     MACRO-11 as well as some additional assignment/replacement  char-
     acters.   The additional assignment or replacement characters are
     listed below:  

               :=             ;This is an assignment or replacement 
                              ;character that implies WORD movement.  

     Example:  

          LET R0 := .PSTPT 

     Moves the WORD represented by .PSTPT into R0.  

               :B=            ;This is an assignment or replacement 
                              ;character that implies BYTE movement.  

     Example:  

          LET R0 :B= @.PSTPT is equivalent to LETB R0 := @.PSTPT 

     In either case, the BYTE that is pointed to by .PSTPT is moved to
     R0.  

     SUPER-MAC  has  some  special operators that are used for bit set
     and bit clear operations.  The operators are listed below:  

     BIT CLEAR OPERATORS      INSTRUCTION GENERATED 

     CLEARED.BY               BIC(B) 

     OFF.BY                        BIC(B) 

     NAND                          BIC(B) 

     Either can be used since they produce the same code.  

     BIT SET OPERATORS        INSTRUCTION GENERATED 



     SUPER-MAC                                                            Page 8



     SET.BY                   BIS(B) 

     ON.BY                    BIS(B) 

     OR                       BIS(B) 

     Either one can be used since they produce the same code.  

     Examples:  

     LET T.FLAG(R2) := T.FLAG(R2) SET.BY #TP.ENB

     LET T.FLAG(R2) := T.FLAG(R2) OFF.BY #TP.ENB

     LET $SYSCL := $SYSCL OFF.BY #CL.NER

     LET (R2) := (R2) NAND R1

     SUPER-MAC  accepts  all  the symbols recognized by MACRO-11.  The
     special symbols utilized by SUPER-MAC are listed below:  

     SYMBOL                   DESCRIPTION

     CARRY                    C BIT (carry bit)

     PUSH                     Keyword for pushing on to stack

     POP                      Keyword for popping off of stack.

     TOP                      Keyword for top of stack.

     GLOBAL                   Keyword for generating a global
                              entry point.

     LOCAL                    Keyword for generating a local
                              entry point.

     SAVREG                   Keyword for saving R0-R5 upon
                              entry into a PROCEDURE

     The  legal binary operators for use in SUPER-MAC are described in
     Table 1-1.  Table 1-1 shows the relationships that can be  estab-
     lished  between expression terms through the use of binary opera-
     tors and also shows the machine instruction  generated  when  the
     macro is assembled.  


                                 Table 1-1
                          Legal Binary Operators

       BINARY                    EXPLANATION        EXAMPLE   MACHINE
     OPERATION
                                 INSTRUCTION



     SUPER-MAC                                                            Page 9



          +  Addition            A + B                  ADD
          -  Subtraction         A - B                  SUB
          *  Multiplication      R0 * #2                MUL
          /  Division            R0 / #2                DIV
     L.SHIFT Arithmetic
             Left Shift          R0 L.SHIFT 1*          ASL
     R.SHIFT Arithmetic
             Right Shift         R0 R.SHIFT 1*          ASR
     L.ROTATE Left Rotate        R0 L.ROTATE 1*         ROL
     R.ROTATE Right Rotate       R0 R.ROTATE 1*         ROR
     SHIFT   Shift
             Arithmetically      R0 SHIFT #2            ASH
     C.SHIFT Arithmetic Shift
             Combined            R0 C.SHIFT #3          ASHC
     XOR     Exclusive OR        A XOR R5               XOR
     NAND    Not AND             (R2) NAND R1           BIC
     OFF.BY                      (R2) OFF.BY R1         BIC
     CLEARED.BY                  (R2) CLEARED.BY R1     BIC
     SET.BY  Inclusive OR        (R2) SET.BY R1         BIS
     ON.BY                       (R2) ON.BY R1          BIS
     OR                          (R2) OR R1             BIS


     * = Number  designates  the  number  of  times the instruction is
     repeated;  i.e., the number of shifts.  

     The legal unary operators are:  

             -                   Negation               NEG 
             NOT                 Complement             COM 

     If  the  assignment  operator  in  a LET statement is not a legal
     SUPER-MAC operator, an error message will be generated.  

     Examples:  

     LET (R2) := (R2) - #1              ;This generates DEC (R2)

     LET (R2) := (R2) - #01             ;This generates SUB #01,(R2)

     LET (R2) := (R2) OR R1

     LET R2 := #0                                                     

     ;This generates CLR R2

     LET R2 := R1

     LET T.VAL(R2) := $VAL2

     LET R0 := R0 L.SHIFT 3

     LET R1 := R1 + #1                  ;This generates an INC R1



     SUPER-MAC                                                           Page 10



     LET R1 := R1 + #01                 ;This generates an ADD #01,R1

     LET R0 := R0 + CARRY               ;This generates on ADC R0


     1.3  Conditional Statements 

     This  category  of SUPER-MAC statements is subdivided into Condi-
     tion Execution statements and Loop Control statements.  



     1.3.1  Condition Execution Statements 

     IF STATEMENT 
     IFB STATEMENT 

     An IF statement causes a conditional transfer or statement execu-
     tion.  The IFB statement forces a byte operation.  

     IF  statements  can  be  either  a  single-line  statement  or  a
     multiple-line (block) statement.  The single-line statement takes
     the form:  

          IF <TEST> [GOTO ]   SUPER-MAC statement 
                    [LEAVE] 
                    [THEN ] 

     THEN  statement  is  not required if GOTO or LEAVE statements are
     used in single line IF statements.  

     The test portion of the IF statement takes the form:  

                    [CC]
                    [CS]
                    [EQ]
                    [GE]
                    [GT]
                    [HI]
     Source         [HIS]
     Destination
     Operand        [LE]
     Operand
                    [LO]
                    [LOS]
                    [LT]
                    [MI]
                    [NE]
                    [PL]
                    [VC]
                    [VS]

     (Note:   these  are  the MACRO-11 branch instructions without the
     "B".  GE not BGE.) 


     SUPER-MAC                                                           Page 11



     A  single  line  statement may have as many arguments as desired,
     provided that all arguments can be completed on the single line. 
     IF $NVAL HI #2 GOTO REJ1 

     IF AND STATEMENT 
     IF ANDB STATEMENT 

     The  AND  statement  is a logical conjunction.  The expression is
     true if, and only if, both A and B are true.  The ANDB  statement
     forces  a byte operation.  AND can only be used with the IF.  The
     form is:  

          A AND B 

     Example:  

          IF (R2) EQ (R1) AND 2(R2) EQ 2(R1) THEN $RETURN NOERROR 

     IF OR STATEMENT 
     IF ORB STATEMENT 

     The  OR  statement  is  a logical disjunction.  The expression is
     true if, and only if, either A or B, or both is  true.   The  ORB
     statement  forces a byte operation.  The OR can only be used with
     an IF statement.  The form of the OR is:  

          A OR B 

     Example:  

          IF A EQ #0 OR A NE C THEN LET A := D 

     The block IF statement requires an END and takes the form:  

          IF...........
            coding
     
          .
     
          .
     
          .
     
          .
     
          .
             coding
          END

     Example:  

          IF A EQ #0 
               LET $VAL2 := T.VAL(R2) 
          END 


     SUPER-MAC                                                           Page 12



     ELSE CLAUSE 

     The ELSE clause is only used with an IF block.  Used in any other
     statement, an error message will be generated.  ELSE  must  stand
     on its own line with no arguments.  

     Example:  

     IF RESULT IS EQ
       LET $VAL2 := T.VAL(R2)
     ELSE
       LET $VAL1 := R2 + #T.VAL
     END

     Multiple  IF  statements  can  be  nested.  Each multiple-line IF
     statement within the nest requires an END.  

     Example:  

     IF .PNUMH EQ #0
       LET $NVAL := $NVAL + #1
       IF $NVAL LOS #2
         IF RESULT IS EQ
           LET $VAL2 := .PNUMB
         ELSE
           LET $VAL1 := .PNUMB
         END
       END
     END
     Special  cases  of  the IF statement perform bit tests.  One case
     tests to determine if the bit(s) are SET and the other  tests  to
     determine if the bit(s) are CLEAR.  

     Examples:  

          IF A SET.IN B THEN...  or IF A ON.IN B THEN...  
          IF A OFF.IN B THEN...  or IF A CLEARED.IN B THEN...  

     Another special case IF statement is a test for zero.  

     Example:  

          IF A GT #0 THEN...  

     A third special case is a test of current condition code setting.
     This is indicated by RESULT IS.  

     Example:  

          IF RESULT IS EQ THEN...  



     ON.ERROR STATEMENT 


     SUPER-MAC                                                           Page 13



     ON.NOERROR STATEMENT 

     Both  of  these  statements  are  special case IF statements that
     check the condition of the C bit.  The ON.ERROR  statement  tests
     to  determine  if  the C bit is set and the ON.NOERROR statements
     tests to determine if the C bit is cleared.  Both statements  re-
     quire  an  END statement if a multiple line procedure is required
     to rectify the problem indicated by the condition of the  C  bit.
     Both statements result in an IF RESULT IS type statement.  

     Examples:  

     ON.ERROR
       IF #CL.NER OFF.IN $SYSCL
         $CALL $MGOUT
       END
       $POSYM
       CLC                    ;Macro instruction
     ELSE
       $POSYM
       CLC
     END

     ON.ERROR LEAVE SETBLK

     ON.ERROR
       PUSH #STSPT
       $CALL $FCSYM
       POP TOP
       ON.ERROR
         LET 16(SP) := 16(SP) + #2
       END
     END

     ON.ERROR
       LET PUSH := T.VAL(R2)
       $CALL $RPREG
       $CALL @(SP)+
       $CALL $SPREG
     END

     ON.NOERROR THEN LET T.FLAG(R2) := T.FLAG(R2)



     LEAVE STATEMENT
     RESTART STATEMENT
     GOTO STATEMENT

     These  statements  are similar in that they transfer program con-
     trol from one point to another point.  Their use and purpose  are
     different.  

     The  LEAVE statement is used when it is necessary to transfer out


     SUPER-MAC                                                           Page 14



     of a program block or loop due to some condition within the block
     or  loop that can be tested.  The test is usually made with an IF
     expression.  

     Example:  

     BEGIN ALPHA
          .
          .
          .
       IF RESULT IS NE LEAVE ALPHA
          .
          .
          .
     END ALPHA

     In  this  example, the result of a previous action is tested.  If
     the result does not equal zero, program control is transferred to
     the expression that follows the END.  

     WHILE A NE B
          .
          .
         coding
     IF C EQ #0 LEAVE LOOP
          .
          .
     coding
     END <WHILE LOOP>

     In this example, if C is equal to zero, the LEAVE will generate a
     branch or a jump outside of the WHILE loop.  

     The  RESTART  statement is used when it is necessary to restart a
     program block or loop due to some condition within the  block  or
     loop that can be tested.  The test is usually made with an IF ex-
     pression.  

     Example:  

          BEGIN ALPHA
            REPEAT
              .
              .
              .
              IF RESULT IS EQ
                RESTART ALPHA
              END
              IF RESULT IS MI
                RESTART LOOP
              END
              .
              .
              .


     SUPER-MAC                                                           Page 15



            END
          END ALPHA

     The GOTO statement creates a branch or jump instruction depending
     on the range.  The target of the BRJ macroinstruction is the  va-
     lue of the symbolic name given by the programmer.  The form is:  

          GOTO name 

     Examples:  

          GOTO SETCM 

          IF A EQ B GOTO SETCM 

     Program control transfers to a routine labelled SETCM.  



     THEN CLAUSE 

     The  THEN  clause  is  used in conjunction with other statements.
     The first statement performs a designated action  and  THEN  per-
     forms a second action.  The THEN clause takes the following form: 

          THEN arguments 

     Example:  

          IF (R2) EQ (R1) AND (R2) EQ 2(R1) THEN $RETURN NOERROR 



     1.3.2  Loop Control Statements 

     FOR and FOR.ABS STATEMENTS 

     The  FOR  statement is a means of controlling loop execution used
     to change the value of an operand by a designated amount until  a
     set  limit  is  reached.   The FOR statement is used with the TO,
     DOWNTO and BY statements.  The form of the FOR statement is:  

          FOR operand [TO    ] limit [BY increment (optional)] 
                 [DOWNTO] 
          END 

     The  default  condition of the increment is one.  The conditional
     branch instruction which controls  the  loop  will  be  a  signed
     branch  when using FOR and an unsigned branch when using FOR.ABS.
     The FOR statement must contain an END statement unless the state-
     ment  is  a  single-line entry followed by a THEN statement.  The
     THEN statement must be followed by arguments:  



     SUPER-MAC                                                           Page 16



     Example 1:  

     FOR A := B TO C BY D
          .
          .
        coding
     END  .

     This  example  causes  B  to be moved to A, D is added to A and A
     compared with C.  If the comparison fails, the loop process  con-
     tinues  until the comparison passes.  The FOR statement is a WORD
     operation statement only.  

     FOR A := B DOWNTO C BY D
          .
          .
        coding
     END

     This  examples  causes B to be moved to A, D is subtracted from A
     and A is compared with C.  If the comparison fails,  the  process
     continues until the comparison passes.  

     Example 2:  

          FOR R0 := R1 TO R2 THEN LET R4 := R4 / #2 

     This  example  causes  the contents of R1 to be moved to R0.  The
     contents of R4 are divided by two and R0 is incremented.  R0  and
     R2  are compared.  If the comparison fails, the process continues
     until the comparison passes.  

     Example 3:  

     FOR R0 := R1 DOWNTO R2
     LET R4 := R4 * #2
     END
     This  causes  the contents of R1 to be moved to R0.  R4 is multi-
     plied by two and R0 is decremented.  The contents of  R0  and  R2
     are compared.  If the comparison fails, the process continues un-
     til the comparison passes.  

          Note well:  FOR and FOR.ABS implement loop control by an INC
     and TST at the bottom of the loop.  The loop will always be  exe-
     cuted at least once and in order to cause the loop to be executed
     10 times, the statements:  

          FOR A := #0 TO #10.
     
          or
          FOR A := #1 TO #11.

     must be used rather than the expected



     SUPER-MAC                                                           Page 17



          FOR A := #1 TO #10.



     REPEAT STATEMENT 
     UNTIL STATEMENT 
     UNTILB STATEMENT 

     The  REPEAT  statement  causes a procedure to be repeated until a
     specified condition is met.  The REPEAT  statement  executes  the
     procedures,  tests  the  specified condition and stops the repeat
     loop when the desired condition is met.  REPEAT statements can be
     single-line   statement   or   multiple   line  statements.   The
     single-line REPEAT takes the form:  

          REPEAT UNTIL condition 

     Example:  

          REPEAT UNTIL (R0)+ EQ (R1)+ 

     This example can best be illustrated by examination of the assem-
     bly code generated.  The assembler generated the following code: 

          B1:;;;;;;  
               CMP (R0)+,(R1)+ 
               BEQ E1 
               BRJ B1                                                 
     ;BRJ IS A MACROINSTRUCTION 
          E1:;;;;;;  

     As  can  be seen the comparison is repeated until it passes, then
     the action stops.  

     There  are  two  types  of  multiple-line REPEAT statements.  The
     first type repeats a procedure until  a  specified  condition  is
     met.   The second type is an infinite repeat (repeat loop) and is
     termiated by an END statement.  

     Examples:  

          REPEAT 
               $CALL C,<R0,R2> 
          UNTIL R4 NE R0 

     The next examples contains a LEAVE statement and was coded within
     a BEGIN block.  

     BEGIN ALPHA
          .
          .
          .
     REPEAT
       $CALL F <FOO,BAR>


     SUPER-MAC                                                           Page 18



       IF RESULT IS NE LEAVE ALPHA
          .
          .
     END <REPEAT LOOP>
          .
          .
     END ALPHA

     The  UNTIL  statement can only be used within a REPEAT statement.
     The UNTIL statement defines the condition(s) that stop the REPEAT
     from looping.  The UNTILB forces a byte operation.  An error mes-
     sage will be generated if UNTIL is used in a statement other than
     a REPEAT.  

     THRU STATEMENT 

     The  THRU statement is used to control loops.  The statement must
     contain an END statement.  

     The THRU statement generates an SOB (subtract one and branch) ma-
     croinstruction.  The statement takes the form:  

          THRU arguments 
          END 

     The first argument must be a register or an expression (LET) with
     a register as the destination.  If the first argument  is  not  a
     register,  an error message will be generated.  The register con-
     tains a number that represents the number  of  times  the  action
     must loop.  

     Example 1:  

          IF R2 HI # 6 THEN LET R2 := #6 
          THRU R2 
               MOVB                                        (R0)+,(R1)+
     ;Note macro instruction 
          END 

     In  this  example,  R2 contains an integer between 1 and 6.  Each
     time the MOVB instruction is executed, the  SOB  macroinstruction
     subtracts one from the contents of R2.  When R2 becomes zero, the
     loop is left.  

     WHILE STATEMENT 
     WHILEB STATEMENT 

     The  WHILE  statement  establishes a condition that permits (con-
     trols) action from other statements.  As long  as  the  condition
     exists,  the action(s) will be permitted.  The form of the state-
     ment is:  

     WHILE condition
       coding


     SUPER-MAC                                                           Page 19



          .
          .
          .
       coding
     END

     The WHILEB statement forces a byte operation.

     Example:

     LET R5 := (R4)+                    ;Get start addr of table
     WHILE R5 LO (R4)
       $CALL DTBL                       ;Go display entry
       LET R5 := R5 + #S.SYCT           ;Get next entry
     END

     $$END STATEMENT 

     The $$END statement supplies an END if those statements are miss-
     ing within nested blocks.  The $$END prints a message on the  as-
     sembly listing for the missing END(S).  The user should check the
     source code to determine if the assembled code  will  execute  as
     intended.   $$END  is  intended for the detection of user "error"
     (i.e., missing END) conditions.  



     1.4  Miscellaneous Statements 

     BEGIN/END STATEMENT 

     The  BEGIN/END statement provides a mechanism for escaping from a
     routine in case some problem develops.  The block of  code  asso-
     ciated with the BEGIN statement is terminated with the END state-
     ment.  The statement takes the form:  

     BEGIN name                         ;Begins a contiguous block
                                        ;of code known as 'name'
     IF RESULT ... LEAVE name           ;A conditional method of
                                        ;escape
                                        ;from 'name'. The branch
                                        ;pointer points to END name.
     ON.ERROR LEAVE name                ;Another method of escape
     END name                           ;End of block.

     Following are two examples of the BEGIN/END statement:

     Example 1:

     BEGIN SETBLK
       $PHSYM                           ;PUSH symbols (macro call)
       $CALL $SCHLT                     ;Search table.
       ON.ERROR
         LET...


     SUPER-MAC                                                           Page 20



         $CALL...
         ON.ERROR LEAVE SETBLK          ;Escape if C bit set.
         IF...
          LET...
         ELSE
          LET...
         END
         LET...
         LET...
         LET...
       END                              ;END of ON.ERROR
       LET
       $POSYM                           ;POP of symbols (macro call)
       RETURN
     END SETBLK                         ;END of SETBLK

Example 2:

     BEGIN ALPHA
            IF...GT...B THEN $CALL...   ;One line IF statement
            REPEAT UNTIL...             ;One line REPEAT
            REPEAT                      ;Multiple line REPEAT

              $CALL...
            UNTIL...EQ...               ;Terminate condition
            $CALL
            REPEAT                      ;REPEAT loop

            $CALL...
            IF RESULT...LEAVE ALPHA     ;One line IF and a LEAVE

            WHILE...IS...THEN...
            END <REPEAT LOOP>           ;End of the REPEAT loop
     END ALPHA                          ;End of the ALPHA block


     SUPER-MAC                                                           Page 21



     $CALL Statement 

     The  $CALL  statement  is used to transfer control (via a JSR PC)
     from one program unit to another.  It may also be  used  to  pass
     parameters  in the registers (R0-R5) between those program units.
     Upon completion of the call, execution is returned to the  state-
     ment following the $CALL.  The form of the $CALL statement is:  

          $CALL NAME <ARGS> 

     NAME  is  the  symbolic name of the program unit being called and
     ARGS are parameters.  ARGS is optional and if  used  must  be  in
     brackets.   If  ARGS  is  used without brackets, an error message
     will be generated.  The ARGS may have six parameters.  The  posi-
     tion  of the parameters within the ARGS brackets indicate the re-
     gister that will contain  that  particular  parameter.   Register
     designations  are  from  left to right, with R0 as the first.  If
     more than 6 parameters are included, a warning  message  will  be
     generated.  

     Examples:  

     $CALL $SCHLT <#$DYNTB,R1> 

     $CALL $FLSYM 

     $CALL DTBL 

     $CALL F <FOO,BAR> 

     In the last example, FOO is moved to R0, BAR is moved to R1 and a
     JSR PC is generated to F.  In the next example, #X  is  moved  to
     R0, #Y is moved to R1, Z is moved to R2 and the JSR PC is to E.  

          $CALL E <#X,#Y,Z> 

     When  macros  are  nested,  ARGS must have multiple brackets, for
     example:  

          IF A EQ B THEN $CALL C <<<R0,#D>>> 

     The  example  shown uses one bracket pair for each statement, one
     pair for the IF, one for the THEN and one for the $CALL.  

     CALLG Statement 

     The  CALLG  statement  (call  with  general arguments) is used to
     transfer control from one program unit to  another  and  to  pass
     parameters  to that program unit via a FORTRAN compatible parame-
     ter block.  The parameter block is built at runtime  and  follows
     the  FORTRAN  convention for null arguments (c.f.  the FORTRAN IV
     and FORTRAN IV+ USER'S GUIDE) and the  argument  count.   General
     purpose  register R5 is first saved, used to point to the head of
     the parameter block on the call out of line,  and  then  restored


     SUPER-MAC                                                           Page 22



     upon  return.   No other registers are used/preserved - it is the
     user's responsibility to  save/restore  registers  as  necessary.
     The  CALLG  statement  may be used to call either FORTRAN library
     routines which expect an R5 call or any MACRO-11 subroutine which
     is FORTRAN callable.  N.B.!!!  in either of these cases care must
     be used in formatting the parameter list in the  CALLG  statement
     to  ensure  that  "CALL BY NAME" is employed rather than "CALL BY
     VALUE".  In most cases this will mean using  immediate  mode  ad-
     dresing  (mode  2  - register 7) in the parameter list.  However,
     the requirement simply stated is as follows:  The parameter  list
     must  be a list of "ADDRESSES" of arguments rather than the argu-
     ments themselves!  The CALLG statement may also be used  to  call
     non-FORTRAN compatible MACRO-11 subroutines in which case the re-
     solution of the "CALL BY NAME " - "CALL BY VALUE" conflict is  at
     the discretion of the programmer.  In all calls the nesting rules
     described for $CALL apply.  

     Examples:

     CALLG SPLAT        ;NO ARGUMENTS - USE ONLY FOR FORTRAN-TYPE
                          ;COMPATIBILITY, ELSE USE $CALL OR CALL

     
     CALLG SPLAT <#ARG1,,#ARG3>

     CALLG SPLAT <#ARG1,,R0,,STIPL>
     

     $RETURN Statement 

     The $RETURN statement is used to return control from a subprogram
     unit to the calling program unit.  The statement allows a  return
     with  status,  with  a register or both.  The statement takes the
     form:  

          $RETURN STA,REG 

     Examples:                Machine Instructions

     $RETURN WITH R5          RTS R5

     $RETURN ERROR R2         SEC
                              RTS R2

     $RETURN NOERROR R5       CLC
                              RTS R5

     $RETURN ERROR            SEC
                              RTS PC

     $RETURN NOERROR          CLC
                              RTS PC

     $RETURN STAT R5          MOVB STAT,-(SP)


     SUPER-MAC                                                           Page 23



                              ROLB (SP)+
                              RTS R5

     $RETURN R4               MOVB R4,-(SP)
                              ROLB (SP)+
                              RTS PC

     $RETURN ,R5              RTS R5


     POP Statement 

     The  POP  statement  is used for POPping WORD data off the stack.
     The statement takes the form:  

          POP P1,P2,P3,...P10 

     The  argument(s)  (P1,P2...)  can  be  any legal destination WORD
     operand or they may be TOP in which case the TOP  (word)  element
     on the stack is POPped into never-never land.  

     Example:                 Generated Code 

          POP R0,R4           MOV (SP)+,R0 
                              MOV (SP)+,R4 

          POP R0,TOP          MOV (SP)+,R0 
                              MOV (SP),(SP)+ 

     The   user  will  note  that  since  MOV  instructions  are  used
     throughout, the CARRY bit is preserved across all POPs.  



     POPB Statement 

     The  POPB  statement provides a similar facility for BYTE data as
     that provided by POP.  The argument(s) (P1,P2...) can be any  le-
     gal destination BYTE operand.  However, they may NOT be TOP.  The
     POPBed byte is always the low-order byte on the top of the stack.
     Remember,  each BYTE POPBed from the stack actually pops one WORD
     from the top of the stack.  



     PUSH Statement 

     The  PUSH statement provides a method for pushing WORD data on to
     the stack.  The statement takes the form:  

          PUSH P1,P2,P3...P10 

     The argument(s) P1,P2...) can be any legal source WORD operand.  



     SUPER-MAC                                                           Page 24



     Example:                 Generated Code 

          PUSH R4,R0          MOV R4,-(SP) 
                              MOV R0,-(SP) 



     PUSHB Statement 

     The  PUSHB  statement  provides a method for pushing BYTE data on
     the stack.  The argument(s) (P1,P2...) can be  any  legal  source
     BYTE  operand.  The PUSHBed operand always occupies the low-order
     byte on the top of the stack with the high-order byte on the  top
     of  the  stack  CLEAR.   Remember,  each  BYTE  PUSHBed  actually
     reserves one WORD on the stack.  



     JUMPTO Statement 

     The  JUMPTO  statement  creates  a  BRJ macroinstruction with the
     pointer pointing to a symbolic name given by the programmer.  The
     form is:  


          JUMPTO name 


     Examples:  

          JUMPTO SETCM 
          IF A EQ B THEN JUMPTO SETCM 

     Program control transfers to a routine labelled SETCM.  
     NOTE:  THEN statement is required syntax in single line IF state-
     ments.  



     CASE(B) Statement 

     CASE(B)  are  statement(s) that will issue a call to a subroutine
     that can be selected by a variable.  CASE(B) must  be  terminated
     by an END statement.  The form of the CASE(B) statement is:  

     CASE(B) variable

     Routine 0
     Routine 1
     Routine 2
     Routine 3
        .
        .
     Routine n


     SUPER-MAC                                                           Page 25



     END

     where:  variable is 0,1,2,3...n 

     The  selector  variable  can  be  any  legal BYTE (CASEB) or WORD
     (CASE) operand that contains the desired number or it can be TOP.
     TOP signifies either the low-order BYTE (CASEB) or WORD (CASE) on
     the top of the stack.  If TOP is used, the TOP word/byte entry on
     the stack is altered.  

     Example:  

     LET R0 := #2
     CASE R0             or        CASE #2
       ADDVAL
       SUBVAL
       ORVAL

     END

     Upon completion of the CASE(B) (END), control will be transferred
     to the ORVAL subroutine.  When ORVAL has finished, i.e., has exe-
     cuted a $RETURN, execution will resume at the statement following
     the END.  The programmer must be careful to validate the range of
     the variable for use with the CASE(B) statement.  (Note:  CASE(B)
     does not generate PIC position independent code).  

     PROCEDURE Statement 

     PROCEDURE  is  a  statement which allows the programmer to impli-
     citly establish an entry point label  for  a  subroutine  (proce-
     dure).  The form of the PROCEDURE statement is:  

     PROCEDURE NAME,TYPE,SAVE 

     where NAME is any legal MACRO-11 label.  TYPE may be assigned ei-
     ther the keyword LOCAL or GLOBAL.  If TYPE is unspecified the de-
     fault is LOCAL.  If TYPE is unrecognizable the default is GLOBAL.
     SAVE may be assigned the keyword SAVREG in which case  R0-R5  are
     saved/restored  upon entry/exit.  If SAVE is unspecified or unre-
     cognized, registers 0-5 are not saved/restored.  

     ENTRYPOINT Statement 

     ENTRYPOINT  is  a statement which allows the programmer to impli-
     citly establish an alternate entry point label for  a  procedure.
     The form of the ENTRYPOINT statement is:  

     ENTRYPOINT NAME,TYPE 

     where NAME is any legal MACRO-11 label.  TYPE may be assigned ei-
     ther the keyword LOCAL or GLOBAL.  If TYPE is unspecified the de-
     fault is LOCAL.  If type is unrecognizable the default is GLOBAL. 



     SUPER-MAC                                                           Page 26



     PROBE and PROBEB Statement 

     PROBE and PROBEB enable the programmer to generate an in line TST
     or TSTB instruction and thus set up the  condition  codes  for  a
     subsequent IF RESULT IS ...  conditional test.  

     BEGINMODULE Statement 

     BEGINMODULE enables a programmer to format a module and track its
     history.  In addition, the BRIDGEPORT-TEXTRON software  copyright
     notice will be appended to the source history.  The form is:  

     BEGINMODULE NAME,IDENT,DATE 


     SUPER-MAC                                                           Page 27



     1.5  Error Messages

     Listed below are some of the error messages generated by
     SUPER-MAC.

     STACK UNDERFLOW!!!

     IF SYNTAX ERROR --- IS

     ELSE SEEN IN OTHER THAN IF BLOCK

     UNTIL SEEN IN OTHER THAN REPEAT BLOCK

     PROCEDURE NAME NOT SPECIFIED

     ENTRYPOINT NAME NOT SPECIFIED

     UNRECOGNIZED 'TYPE' KEYWORD - DEFAULT TO GLOBAL

     UNRECOGNIZED 'SAVE' KEYWORD - REGISTERS NOT SAVED

     --- MUST BE A REGISTER

     --- STRANGE SUPER-MAC STACK VALUE

     --- ...ARGS MUST BE WITHIN <>

     --- NOT A LEGAL ASSIGNMENT OPERATOR

     6 ARG MAX (R0-R5)

     --- NOT A LEGAL OPERATOR

     NO CODE GENERATED



     SUPER-MAC                                                           Page 28



     $$END statement   19

     $CALL statement   21

     $RETURN statement   22



     AND(B)   11

     ASSIGNMENT statement   6



     BEGIN/END statement   19

     BEGINMODULE statements   26

     BINARY OPERATORS   8

     BIT TESTS   12



     CALLG statement   21

     CASE(B) statement   24

     CONDITIONAL statements   10



     ELSE clause   12

     ENTRYPOINT statement   25

     ERROR MESSAGES   27



     FOR and FOR.ABS statements   15



     GOTO statement   15



     IF STATEMENT   10

     IFB statement   10

     INTRODUCTION   5



     SUPER-MAC                                                           Page 29
INDEX


     JUMPTO statement   24



     LEAVE statement   13

     LET(B) statement   6

     LOOP CONTROL statements   15



     MISCELLANEOUS statements   19



     ON.ERROR statement   12

     ON.NOERROR statement   13

     OR(B)   11



     POP statement   23

     POPB statement   23

     PROBE and PROBEB statement   26

     PROCEDURE statement   25

     PUSH statement   23

     PUSHB statement   24



     REPEAT statement   17

     RESTART statement   14



     THEN clause   15

     THRU statement   18



     UNARY OPERATORS   9

     UNTIL statement   18



     SUPER-MAC                                                           Page 30
INDEX


     WHILE statement   18

     WHILEB statement   19