RUNOFF INTERNALS                                                        Page 1



                               RUNOFF INTERNALS


This  is  a  quick guide to RUNOFF for those who wish to modify it.  It is in-
tended as a guide and not  a  complete  explanation.   The  novice  programmer
should  confine changes to those documented in the BUILD file.  Since all mod-
ules are heavily commented the comments are a more detailed guide.  

                                 MACRO modules

     1.  RNODYN  - Dynamic memory routines.  These store character strings for
         use by RNO.  The routines essentially simulate a sequential file with
         access by record number.  
              1 Record = 1 byte 
         You  should  learn  how  these routines work it you wish to implement
         changes.  

     2.  FMTCM  - This contains all special purpose routines to format output.
         This inclues chapters, lists, notes, and header levels.  

     3.  GCIN - Contains all character interpretation routines.  

     4.  RUNOFF  -  Main  program  with  line  formatting  routines, and input
         parameter parsing routines.  

     5.  CMTAB - Command tables - defines commands and routines they call.  

     6.  COMND - Command parser 

     7.  ERMSG - Error message routines and messages 

     8.  HYPHEN - Autohyphenation routine 

     9.  ESCAPE - Contains all DEFINE, DELETE, RESET commands.  

    10.  INDEX - Contains indexing routines 

    11.  INIT - General initialization and all flags commands.  

    12.  PINDX - Contains index printing routines 

    13.  RNCMD  - General purpose commands- skip, page, indent, footnote, text
         etc.  

    14.  RNORSX - RSX I/O tables 

    15.  RSXIO - I/O routines for RSX 

    16.  RTIO - RT-11 I/O routines.  

    17.  RNORT  -  RT-11  startup.  These are include command line parsing and
         .REQUIRE commands.  

    18.  START  -  RSX  specific file parsing routines.  Includes command line
         parsing and .REQ commands.  



RUNOFF INTERNALS                                                        Page 2



    19.  STYLE - Contains most style, layout, and display commands.  


                             Structure of program

     1.  Certain register conventions are used throughout:  
       R0 - is completely volatile.  It can not be trusted on return from sub-
         routines unless otherwise stated.  
       R1 - is  completely  volatile.   It  is  often  used  to be the current
         chacter.  
       R2 - is  preseved  in  general across subroutine calls inless otherwise
         stated.  
       R3 - points to a header for a buffer chain as defined in RNODYN.  
       R4 - is preserved.  It points to the numeric input routines when a com-
         mand interpretation routine is called.  
       R5 - is preserved across calls.  
       C  - is generally clear if the call is ok, and set if not.  

              The command interpretation routines are not assumed to save, re-
         store any registers, so they have free use of all registers.  Not all
         routines  use consistent conventions, because I started with an older
         verstion from DECUS.  

     2.  A  stack  structure is used for all input.  This is the heart of this
         program.  A set of headers are used to point to various places in the
         input.   Whenver a substitution is made, the stack depth increases by
         1 header.  Some routines such as the chapter routine call  SETINS  to
         increase the stack depth and then add strings to input, then standard
         routines are used to format the output.  There is a big trap for  the
         unwary  here.   When  the  stack depth is increased, the user may add
         data to the end of input, and when the stack depth is decreased,  the
         added data evaporates.  

              At stack depth 0 only the input line read from the input file is
         available, but at higher stack depths the substitution buffer is used
         as input.  

     3.  The character width is now variable.  To get the width you should use
         the character width routines in GCIN.  

     4.  The  number  conversion  routines  accept  input on the stack.  These
         routines wish to find a series of numbers terminated by a zero  word.
         The output is put into the buffers pointed to by R3.  

     5.  All  input is parsed, by discarding all control characters except for
         TAB, CR, and LF.  Each input line ends with CR,LF.   Fake  input  may
         end with only LF.  

     6.  The  input  interpretaion in GCIN is table driven.  There is a set of
         tables defining the characteristics of each character.   The  charac-
         teristics  table  defines  autobreak, flags, period, and underlinable
         characters.  Characters are marked as available as non  alphanumeric,
         and  as to availability for use as a flag.  Another table defines the
         disposition of each character.  The disposition  table  points  to  a
         vector table which dispatches to a specific routine.  The disposition
         table is modifiable by the FLAGS commands.  The definition  table  is


RUNOFF INTERNALS                                                        Page 3



         modifiable by the FLAGS, PERIOD, AUTOBREAK, AUTOHYPHENATE, and UNDER-
         LINE commands.  Upper/lowercase characters are distinguished  by  the
         entries in the disposition table.  The values 0 and 2 mark the possi-
         ble values.  All values are symbolic.  Two values  are  used  in  the
         disposition  table,  negative and positive.  Positive defines allowed
         input characters, negative are characters that trigger an  action  on
         output,  and  are  not  printed.   This  keeps the table sizes small,
         though the program is a little slower.  

              An  additional  table  of  character  widths  has  been added to
         facilitate proportional fonts.  

     7.  Most  error  messages call ERMSG, except when overlay switching could
         be fatal.  Then imbedded messages are  used.   ERMSG  contains  error
         messages  and since it is in a separate overlay the messages are only
         availabel when ERMSG is called.  

     8.  The initial stack pointer is saved, and periodically restored.  After
         each fatal error and before each new line of input  it  is  restored.
         This simplifies stack cleanup.  

     9.  If you make major changes in RNO you should enable the symbol $DEBUG.
         This attempts to catch bugs by checking the dynamic buffer  structure
         in  RNODYN.  In addition it creates a routine called CHROUT which may
         display the current value of R1.  You  may  then  sprinkle  calls  to
         CHROUT in your routines to view the character being handled.