Sort-11 with RMS resident library                                        Page  1
B. Z. Lederman


          To  build  V3.0 with the RMS supervisor mode library, create a new ODL
     file by editing the SRTUTL.ODL file.  Locate the following lines:  

     ;  overlay all links
     ;
     SRTOVR:    .FCTR   *(SLINK1,SLINK2,SLINK3,SLINK4,SLINK5)

     Remove  all  of  the RMS references which follow until you get to the .ROOT
     line.  Then insert the following, and edit the .ROOT  line,  to  look  like
     this:  

     ;
     ;  reference RMS
     ;
     RMSROT:    .FCTR   LB:[1,1]RMSLIB/LB:R0AUTS:R0EXSY:R0IMPA
     ;
     ;  the final task
     ;
        .ROOT   SRTROT-RMSROT-SRTOVR
     ;
        .END

     Linking  to resident libraries (since RMS V2.0) is usually much easier than
     using disk overlays.  If you do not have supervisor mode,  then  R0AUTS  is
     replaced  with  R0AUTL, but you will not obtain as much benefit as you will
     with the supervisor mode library (there might even be a loss of task  image
     space,  depending on the disk overlay structure used).  Next, create a task
     build file like this (this example assumes the above  ODL  file  was  named
     SR4.ODL):  

     ;
     ; This command file is used to task build the PDP-11 SORT  Utility Program
     ;
     SR4, SR4 = SR4/MP
     ;
     TASK=...SR4
     ASG=TI:1
     UNITS=24
     RESSUP=LB:[3,54]RMSRES/SV:0
     ;
     ; The next line defines the size of the task by setting the size of the
     ; sort work PSECT
     ;
     EXTSCT=SORAAA:120000
     ;
     //

     I  named  the task SR4 during testing, but when normally installed the task
     name becomes the normal name of ...SRT.  The EXTSCT should be  set  to  the
     largest  value  which  will  not  run  the  task up over 32Kwords (the task
     builder will give you a warning that the task has illegal  addresses).   If
     you  do  not have supervisor mode, you will have to reduce the value of the
     EXTSCT and replace the RESSUP option with  LIBR=RMSRES:RO.   I  have  tried
     Sort-11 with the non-supervisor mode library on a PRO-350, and it works.  



Sort-11 with RMS resident library                                        Page  2
B. Z. Lederman


          In  case  anyone  wants  to experiment with the I-and-D space version,
     this is the task build command file I used:  

     SORTID/-FP/ID, SORTID/-SP =
     ;
     SRTLIB/LB:$ALLOC:$BILDR:$CDINP:$CLEMH:$CLSSF:$CMIO1:$CMIO2:$CMIO3
     SRTLIB/LB:$CMPRS:$DCNSF:$ENDIO:$GETST:$GSAHN:$IMDAT:$INCMP:$MSGHN
     SRTLIB/LB:$NDBLD:$OPNIO:$OUTIO:$OUTSF:$PRSMS:$PRTAB:$PRTST:$RDINP
     SRTLIB/LB:$RFARD:$RSTSF:$SFINI:$SFINP:$SFOUT:$SFSWP:$SMEND:$SMGSA
     SRTLIB/LB:$SMINI:$SPCIN:$STMRG:$STRLS:$STRTN:$UTEXT:$VCCLB:$VCCMP
     SRTLIB/LB:$VCINI:$VCWRN:$WRNHN:$WTEXT:B16ABS:B16CH1:B16CH2:B16CH3
     SRTLIB/LB:B16CH5:B16FTN:B16PG2:B16PG4:B16SAV:B16STP:CALLBK:CC$CON
     SRTLIB/LB:CINITL:CMPA:CMPB:CMPC:CMPD:CMPF:CMPI:CMPJ
     SRTLIB/LB:CMPK:CMPL:CMPP:CMPS:CMPU:CMPZ:COLL$U:FTREE
     SRTLIB/LB:GCMBLK:GETCM:GETCMD:GETMRG:GETREE:GFS$GE:ICT$IN:INMRG
     SRTLIB/LB:KEYCMP:MNCTG:P1$PAS:P2$PAS:P3$PAS:P4$PAS:P5$PAS:PC$PAR
     SRTLIB/LB:PI$PAR:PK$PAR:PM$PAR:PRSCOL:PT$PAR:SCOUT:SDECM$:SINITL
     SRTLIB/LB:SMMAIN:SOR$$C:SOR$CO:SRTSGE:SRTSPC:SRTWRN
     ;
     LB:[1,1]RMSLIB/LB:R0AUTS:R0EXSY:R0GCML:R0IMPA
     ;
     LB:[1,1]RMSLIB/LB
     /
     TASK=...SRT
     ASG=TI:1
     UNITS=24
     RESSUP=LB:[3,54]RMSRES/SV:0
     ;
     ; The next line defines the size of the task by setting the size of the
     ; sort work PSECT
     ;
     EXTSCT=SORAAA:124500        ; SORT EXTENSION
     ;
     //                                                                         
        

     This can be built to the non-supervisor mode RMS library, or to no resident
     library, and will still have the  same  amount  of  task  work  space  (the
     resident  libraries  take  up  Instruction space only).  Using the resident
     libraries will reduce the size of the task  image,  however  (this  version
     uses  up about 54Kwords of memory, and increasing the EXTSCT to 140000 uses
     up  about  58Kwords).   This  version  appears  to  perform  all  functions
     properly:   increasing  EXTSCT to 140000 results in a task which sorts, but
     will not write out internal statistics properly when the /SS switch is used
     (the  numbers appear properly, but with no text labels).  Increasing EXTSCT
     to 160000 yeilds a task which builds properly, but will not execute.  

          I  have  not  saved  my  old  V2.0  build  files,  but  converting the
     distributed files to build with the RMS supervisor mode library follows the
     same  procedure as for V3.0:  remove all disk overlays which reference RMS,
     put in a new RMSROT as shown in the above ODL file (you may  also  have  to
     include module RMSSYM:  look in LB:[1,1]RMSRLX.ODL for an example), and use
     the RESSUP option in the build command file.  In general,  any  task  which
     uses  RMS  can  be converted to use the supervisor mode resident library by


Sort-11 with RMS resident library                                        Page  3
B. Z. Lederman


     following these steps, and I have even converted tasks which  normally  use
     FCS  to  use the RMS library in this manner.  I do not recall any instances
     where the task failed to build and operate properly with the RMS supervisor
     mode  library  (if  the  task  worked correctly to begin with, and no other
     changes were made, such as removing  overlays).   You  will  also  have  to
     adjust  the EXTSCT command in the build file to expand the task image so it
     is just under 32Kwords, to obtain the maximum benefit.