LOADABLE DEVICE DRIVER DATA BASES
                            IN RSX11M SYSGEN
                                    
                           Carl T. Mickelson
                     Goodyear Aerospace Corporation
                           Akron, Ohio 44315



                                ABSTRACT
                                ________In order to support multiple and differing configurations of peripherals
on different computer systems, a method for modifying RSX11M SYSGEN is
discussed that allows device drivers to be built with loadable, rather
than resident, device data bases.  System tailoring is done at VMR-time
when the particular devices for each configuration are included in the
bootable system image.  The method allows the addition of new devices
without a new SYSGEN. 




                              INTRODUCTION

What do you do when your OEM employer's business is growing and he
acquires a room full of new computer systems for a variety of different
customers?  Each system has a different configuration of discs and
terminal interfaces and you are expected to provide a consistent
software development environment on all these different systems so that
user's may build programs on any development system and move them to any
test stand system to check out your product hardware.  The users don't
want to be confronted with different operating procedures on each
machine and would like to move even privileged tasks, when possible,
from system to system without re-building them.  In addition, you don't
want to be confronted with performing a new system generation for every
new system as it arrives. 

It would be much more convenient to maintain a system generated for each
generic processor (11/34, 11/24, 11/40, 11/70) and memory configuration
and simply build an operating system for a new computer by selecting an
existing pre-generated system and specifying what devices are in the
configuration at VMR time.  Further, the tailoring of the terminal
driver for different systems raises an additional complication for
systems having the same processor but differing terminal I/O
controllers. 

This paper discusses a method of achieving this degree of
hardware/software independence for RSX11M, and discusses how this goal
to provide a common operating environment was achieved.  It should be
noted that privileged tasks that map over the Executive can still only
be ported between systems with the same or similar processors and the
same memory address range (18 bit or 22 bit).  This represents an
improvement over "vanilla" RSX11M since device configuration is no
longer a consideration. 

                      ISSUES NEEDING CONSIDERATION

The principal method needed to achieve the goals stated above is to
modify the RSX11M SYSGEN procedure to make all DEC supplied device








drivers look like user-written drivers, each task-built containing its
own loadable device data base structure.  By doing this, device data
structures are no longer resident in the Executive task image
(RSX11M.TSK), and individual devices can be configured into a system by
loading their data bases, together with their driver code at VMR time. 
In fact, the only device drivers that need to be present in the bootable
system image are the boot device and terminal device drivers.  All
others can be loaded into GEN with a /HIGH switch in the system startup
file.  The ability to add additional devices is also enhanced, since a
SYSGEN can now be avoided.  There are, however, a number of issues that
must be addressed in order for this technique to be successful. 

First, all link time references to I/O data structure symbols must be
eliminated, since the I/O data structures are no longer resident in the
Executive.  Without doing this, the link time references to .TT0 and
.CO0 in the Executive (SYSCM) and any privileged tasks such as the Pool
Monitoring Task (PMT) and the Console Output Task (COT) will produce
undefined references when they are task-built. 

This requirement is satisfied by adding some code to the Executive
module INITL.MAC to walk down the device DCB chain when the virgin
executive is initially started to locate .TT0, the console terminal UCB
address, and .CO0, the console output UCB address.  Once found, these
addresses are loaded into the required fields of SYSCM, and RSX11M
continues as if the data bases were resident.  Similar code is added to
PMT and COT at their entry points, and the references to these symbols
are made indirectly to local copies of the addresses.  This isolates
these privileged tasks from the actual locations of the data structures. 

Second, the Executive module SYSTB.MAC, generated by SYSGEN during the
device configuration phase, must be split into individual files
(xxTAB.MAC), one for each type of device selected for inclusion in the
SYSGEN process.  The only data structures remaining in SYSTB are the
pseudo-device structures for SY:, LB:, etc, and the clock queue
list-head.  The device data base files must later be assembled with the
RSX11M driver sources, so additional commands must be added to
RSXDRVASM.CMD.  Also, the driver task build command file, RSXDRVBLD.CMD,
must be modified to task build each driver with its own local data base. 

Finally, to support different configurations of terminal interfaces on
systems with similar processors, a method must be found to build
multiple versions of the terminal driver.  Each version of the driver
must have a loadable data base structured for that particular system so
that the driver for the proper terminal configuration can be loaded at
VMR time.  It is assumed that the full-duplex terminal driver is the
driver of choice for this effort as it provides full system
functionality for the user. 

                         DEVELOPING THE CHANGES

Once it is understood what must be done, a method must be developed to
automatically apply the changes when a system is to be generated.  This
method should be applied in two parts. 

The first part applies the needed changes to SYSCM and the privileged
tasks to eliminate the link time references discussed earlier.  These
changes are required for the SYSGEN changes to be successful, but they
can stand alone so that the tasks do not directly access I/O structures








at link-time. 

The second part of the modification package should apply the changes to
the SYSGEN procedure files, and should only be applied if the first part
changes are made.  These modifications amend the SYSGEN procedure to
achieve the functionality described earlier. 

In order the develop the changes, a number of utilities are necessary,
among them the standard utilities SLP, PIP, MAC, TKB, etc, and a DECUS
supplied disassembler DOB.  This utility is needed to disassemble
certain modules, delivered only in object format so that they may be
modified in source form, re-assembled and re-inserted into their
appropriate object library. 

A trial SYSGEN was performed, stopping at all end of section and end of
execution breakpoints to study the state of the files produced by
SYSGEN.  The SYSGEN command files themselves were examined to determine
where changes had to be made and a set of command procedure (.CMD) and
source update (.SLP) files were developed to apply the changes
automatically.  The specific modifications made to the SYSGEN procedure
are discussed below. 

                        SYSGEN PROCEDURE CHANGES

The default option for all device drivers is set loadable, and this
specific question is eliminated from the SYSGEN dialogue.  The need for
this is self-evident since the desired goal is to make a system with
loadable device data bases.  Also, the user is given the opportunity to
include the Executive routines $PTWRD and $GTWRD regardless of whether
user-written device drivers are to be included during the system
generation.  This is done to insure that these routines are available if
a user-written driver will be incorporated at some future time. 

Additional questions are added to the procedure to allow the user to
establish an identifier (xxx) for each specific version of the terminal
driver and system executive configuration being simultaneously generated
for a common processor type.  This identifier is appended to the
terminal driver task and symbol table file names, and to the Executive
symbol table and bootable system file names to designate the system
configuration pertinent to each set of files. 

A tailored system VMR command file (SYSVMRxxx.CMD) is generated for each
individual system configuration, and the user is given the opportunity
to specify the device drivers that should be included in the system
image prior to the first bootstrap.  The balance of the VMR file is
tailored to install only those privileged tasks needed for support of
the devices loaded into the system image.  Thus, if DUDRV is loaded, RCT
is installed, and queue manager support is included only if LPDRV has
been loaded. 

Finally, just before VMR is invoked to create a bootable image, the user
is permitted to select the version of the system and hence TTDRV version
to be used to create the bootable system image for the SYSGEN host
system. 

The modified procedure, when completed through Phase II creates a set of
virgin system (RSX11Mxxx.SYS) files that can be moved to another disc
medium and together with the drivers and privileged tasks in [1,54],








libraries in [1,1] and other system directories such as [1,2] can be
used to VMR another system for a different hardware configuration.  The
resulting system can be booted on the new system configuration and has
the same Executive and resident library characteristics as the
originally VMR'ed system. 

                       USING THE MODIFICATION KIT

The modifications described here are performed by a set of command
procedures that will be available on the RSX SIG tape from the New
Orleans DECUS.  They should be used in accordance with the following
procedure. 

First copy the RSX11M baseline distribution kit to scratch media as
described in the RSX11M SYSGEN reference manual.  Then apply DEC's
distributed Update D patch procedure to recreate the RSX11M baseline kit
against which these modifications are performed.  If the Able Computer
Technology ENABLE Memory Management Unit (and Cache) is to be installed
in your host system, apply the Able supplied patches next.  Remember
that any system built with the ENABLE hardware support cannot be moved
to a system without the same hardware.  This is a restriction of the
Able patches, and not the changes discussed here.  Finally, apply the
procedure described in this paper by invoking the DECUSMODS.CMD command
procedure. 

This command procedure supports all three types of RSX11M distribution
kit and will ask the user to specify which kit is in use.  The procedure
will then ask the user to re-build the indirect command processor (ICP)
to enlarge its symbol table if a very large system configuration is
being generated.  This step should be taken, and the new ICP installed
if the SYSGEN being performed will generate a system with a very large
number of devices. 

DECUSMODS should be re-invoked to apply the modifications described
here.  A set of hexadecimal modifications can be installed by this
procedure if the user wishes.  These hex modifications are discussed in
the companion paper "RSX11M Hexadecimal Command Line Numerics" presented
at this DECUS symposium.  The next set of changes that can be applied
are the first part or I/O symbol linkage changes discussed earlier. 
These must be selected if the loadable driver data base changes are to
be applied. 

Each set of changes will be applied in sequence as the user selected. 
The procedures are designed to verify the modified files against
expected results, but due to DECUS restrictions about copyrighted source
code content on SIG tape submissions, not all the required files can be
included.  This should pose no problems, so long as Update D of V4.1 is
used as the baseline for the procedure.  After the modifications are
performed, the normal SYSGEN procedure is initiated as described in the
SYSGEN manual. 

                    DIFFERENCES IN SYSGEN PROCEDURE

The following procedural changes should be observed when performing a
SYSGEN with these changes applied. 

If the system is autoconfigured, and the autoconfigure results are not
overridden and amended, the resulting system will be restricted to








supporting only the devices found by the autoconfigure program.  This
defeats a major purpose of using these changes, that is to generate a
single system capable of supporting many different hardware
configurations. 

If autoconfigure is suppressed or overridden, when SYSGEN asks for the
number of controllers of each device type in the system, the user should
specify the controllers that comprise the union of all controllers in
all the systems to be supported.  Thus if three systems are to be
supported on three different systems disc types, the controllers for
each disc should be specified in the hardware configuration section. 
The number of each controller type to be generated should be specified
as the maximum across all the systems to be supported.  By following
these two rules, SYSGEN will build all the device drivers necessary to
support all the systems and will generate data bases to support the
largest hardware configuration.  Smaller systems will indicate off-line
status for those devices not present at boot-time. 

The same rules pertain to specifying the number of terminal controllers
YL, YH, YZ, etc during the system hardware configuration.  Later during
the procedure, where each system's terminal driver is configured, the
procedure will permit the user to specify the actual number of each
controller type supported by a given system configuration.  This is
where each TTDRV data base is reduced in size to support only the
specific terminal interfaces present in a system. 

A word of caution applies here however.  If the maximum number of any
specific terminal interface class (YL, YH, YZ, etc) is greater than one,
the minimum number that should be specified during this tailoring phase
is either 0 (none) or 2 controllers for that class.  This is
particularly important for the YL class of single line controller.  If
this rule is not followed, the driver will assemble for a
multi-controller system configuration, but the LOAd processor will
create an Interrupt Transfer Block (ITB) in POOL to support only a
single controller.  If this should happen, the generated Executive will
CRASH ON THE FIRST KEYSTROKE after the virgin Executive is bootstrapped! 

The SYSGEN procedure continues normally, configuring Executive, terminal
driver and other system features.  During the device configuration
phase, where CSR and vector addresses are specified for each device
controller, when the terminal devices are being configured, the modified
procedure asks for the system identifier discussed earlier.  The
procedure then asks for the number of each type of terminal controller
in the system.  The procedure creates a terminals data base containing
the currently specified subset of controllers and asks if another driver
data base is to be built.  If another is to be built, a new identifier
and controller set is requested and the new data base is created.  This
process is continued until no more data bases are requested. 

During this section, if the first system identifier specified is the
NULL string, a standard single configuration system is built, including
support for loadable data base device drivers.  A non-null string causes
a tailored terminals data base (TTTABxxx.MAC) to be created for the
system. 

Phase I of SYSGEN continues normally, assembling the Executive, drivers
and individual driver data bases and preparing for Phase II task
building.  Chaining to Phase II continues the SYSGEN procedure where the








system libraries, Executive and privileged tasks are built.  It is
during this phase that the modified procedure asks the user to
re-specify the list of system identifiers used to designate the
different terminal driver configurations.  This list is used to create a
virgin system boot file for each individual system configuration.  In
addition, the user is given the opportunity to specify a list of device
drivers to be installed in each system.  This list of drivers is used to
tailor a SYSVMR file for each system configuration.  At the end of this
stage, the user is asked to specify the system identifier for the system
on which the SYSGEN is being performed.  The proper version of the
terminal driver is selected for for inclusion in the host's new system,
and the system VMR process is executed to configure the new operating
system for the host machine.  When Phase II of SYSGEN ends, the new
Executive is booted and saved with the bootstrap block written in the
usual manner. 

When the system re-boots itself, SYSGEN Phase III can be performed to
re-build any needed utilities to use RESLIB, ANSLIB or other system
features.  After completing Phase III, and purging the system disc, the
system is ready to be transported to another hardware configuration. 

                MOVING TO ANOTHER HARDWARE CONFIGURATION

To move the newly generated system to another hardware configuration,
the following minimum set of directories and files should be copied to a
new system disc device, ([1,1], [1,2], [1,54], [11,10]RSXMC.MAC). 

Directory [1,1] contains the system object and macro libraries; [1,2]
contains the help files and standard startup procedure files; and [1,54]
contains the system privileged tasks and utilities.  RSXMC.MAC is
included to provide definitions of the supported system features so that
privileged tasks needing this information can be assembled correctly. 

The correct version of the terminal driver task image and symbol table
should be copied from TTDRVxxx.* to TTDRV.* and VMR executed using
SYSVMRxxx.CMD to configure the bootable Executive for the new system. 
The new system image RSX11Mxxx.SYS sholud then be bootstrapped and saved
with bootblock to create a system disc that is bootable on the new
configuration. 

This new system has exactly the same Executive, resident libraries,
privileged tasks, and utilities as the original system.  Further,
neither system has suffered a loss of dynamic storage or POOL space due
to un-necessary device data structures resident in the Executive.  Also,
the terminal driver has been tailored to support the specific kind and
number of controllers on each hardware configuration. 

                          ADDING A NEW DEVICE

Adding a new device to a system built with these changes is a relatively
easy job.  There are a number of different cases that need to be
considered, but the job can typically be accomplished without the need
of another full system generation. 

If a device is to be added on an existing controller, the procedure is
as follows.  First, the data base source file xxTAB.MAC is edited,
adding a new UCB structure to the file.  The new UCB is added to the end
of the existing UCB's in the file and is linked to the DCB and SCB








already present.  The highest unit number field of the DCB is
incremented to enable the new unit. 

The revised file is re-assembled with RSXMC.MAC and EXEMC.MLB to produce
an object file for the new data base.  The driver task and symbol table
are re-created by task-building the new data base with the driver code
object file.  The new driver is placed in service by simply LOAding it
at system startup if it was not installed by VMR.  Otherwise, a copy of
the virgin Executive, RSX11M.TSK, must be reinitialized with VMR and
re-booted to install the new driver. 

Installing new devices on a new controller is a similar procedure,
except that a new SCB together with the UCB(s) must be added to the data
base.  Additional information on performing these steps can be found in
the Guide to Writing a Device Driver in the sections describing how the
I/O data structures are organized. 

If a new type of device is to be added to the system and the system was
originally generated anticipating the device's inclusion in the
configuration, this task simply entails LOAding a driver that is already
available.  If a pre-built driver is not available, the data structure
for a similar type device could be used as a model for the new device. 
However, this approach is difficult to accomplish successfully except in
the simplest of cases for straight forward devices.  The approach breaks
down if the device UCB is extended to include device specific fields. 
In this case, the driver should be built during the SYSGEN procedure. 

                        CONCLUSIONS AND COMMENTS

The techniques discussed here and embodied in the files of the
modification kit permit multiple configuration systems to be generated
simultaneously, with fully loadable device drivers and data structures. 
This permits a running system to be expanded easily and can eliminate
the need to do an additional SYSGEN to make simple system configuration
changes. 

These techniques have been successfully used to generate systems
supporting PDP 11/34, PDP 11/24, and PDP 11/40 UNIBUS processors. 
Systems with both 18 and 22 bit address support have been built from big
disk, RK06/RK07 and RL02 distribution kits.  The following cautions and
caveats are applicable when considering using these changes: 

1. Controller CSR and vector addresses must be consistently set across
all systems.  SYSGEN'ing different types of controllers at the same
address is acceptable as long as their device drivers are not LOAded
into the same system image during VMR processing or system operation. 

2. Support for multiple terminal driver configurations is provided for
the full-duplex terminal driver only. 

3. The changes apply to Update D of RSX11M V4.1.  Proper application to
other updates of V4.1 is not guaranteed.  Since Update D added DEUNA
driver support to RSX, and changes are made in building its data base,
earlier Update kits are known to be incompatible with the changes. 

4. Laboratory devices (A/D and D/A converters) and the IC series devices
have not been addressed.  Since the systems at the author's site do not
use these types of interfaces, no changes have been designed for these








devices during SYSGEN. 

5. Any layered product that expects to find some I/O symbols defined in
the Executive symbol table will not link successfully.  This applies
only to layered products that are built as privileged tasks as they are
the only ones with the potential to access these I/O structures
directly. 

6. The compilers in use at the author's site have been built and used
without modification.  DECnet, however, has not yet been added to these
systems, so it is not known if the changes will effect the NETGEN
procedure.  Inclusion of DECnet in these systems is planned for the near
future. 

7. While the changes made to the SYSGEN procedure do not depend upon the
processors being UNIBUS based, no Q-bus machine configurations have been
generated.  It is not known if these changes will properly support a
Q-bus based system. 

8. Last, but not least, it must be remembered that systems generated
using this procedure are transportable only between multiple hardware
configurations that share the following characteristics: 

   a. same or similar processors; if built for EIS support, all
   processors must support EIS. 
   
   b. have memory management hardware; must be mapped systems to provide
   the support necessary for loadable device drivers. 
   
   c. same memory address range; if built for 22 bit extended memory,
   all systems must support 22 bit addressing. 

                                 CAVEAT

The kit of files comprising the SYSGEN changes described here are
supplied for information purposes only.  Use of these changes at any
PDP-11/RSX11M site is entirely at the risk of the using organization. 
Neither the author, nor Goodyear Aerospace Corporation, nor DECUS, nor
the RSX SIG is responsible if these changes do not perform successfully
in any particular system.