Documentation for CPU Monitor for RSX11-M/M+

        Don Rubin
        S.E.T. Inc.
        9703 Forest Glen Court
        Silver Spring, MD 20910

     The  enclosed  program  is  a  graphic  CPU monitor for
RSX11M/M+.  It requires no  modification  to  the  operating
system  and  adds  little  overhead  to  the system.  It was
created because there is no way to measure CPU  availability
in RSX (the stuff on the RMD system page is garbage, ask the
DEC developers).  

     The program works as follows:  

      .  it is installed at priority 200 (though 50 would be
         OK) 

      .  after  initialization it hangs a 1 second mark time
         and drops to priority 5 at which point it is higher
         than  the null task but lower than every other task
         in the system 

      .  at the low priority it increments a counter 

      .  when  the  mark time expires the priority is raised
         and the CPU availability is computed and  displayed
         on a bar graph (VT100) 

      .  the  counter is cleared, another mark time is hung,
         and priority dropped 

      .  program  is terminated by the user typing any char-
         acter on the terminal the program is running from 


     In  our  application  we  have a version of the program
which doesn't display the data directly but dumps it into  a
global common for display by another task.  The program must
be calibrated for each particular system.  To calibrate  run
the  program with the command "CPU CALIB" which causes it to
dump calibration values.  Pick the average value (make  sure
the  system  is quiescent at this point).  After calibration
the value may be hard coded into the program or  entered  in
the command line "CPU 115000".  

     The  program can be built as follows (note, source, ob-
jects and task supplied) 

        f77 cpu=cpu/-wr
        mac mymark=mymark
        mac ast=ast

                                                      Page 2



        tkb cpu/fp=cpu,mymark,ast,lb:[1,1]f4pots/lb
        ins cpu/task=...cpu/pri=200

     The  program  as  supplied displays CPU utilization but
can be changed to show availability by subtracting the util-
ization  from  100 before display.  I can answer written in-
quires only at the above address.  

                                                        Don
Rubin