xmt - intercomputer communications task
                                                                  12-Jan-82
 
 
                                      Overview
                                      --------
 
 
 
          XMT is a utility task which provides a convenient means for  data
          transfer between the the Medical Physics PDP11 and any other com-
          puter system that is accessible with a standard terminal  by  ei-
          ther hard-wired lines or by dial-up modem.  XMT makes your termi-
          nal appear as though it were connected directly to  the  "remote"
          computer system.  Data transfer is performed by producing textual
          output from the remote computer (e.g., program listings, computer
          runs, etc.) and, through XMT, routing that text to a disk file at
          the PDP11.  The reverse path  takes  a  file  at  the  PDP11  and
          "types" it to the remote.


          
                                                                  12-Jan-82
 
 
 
 
 
 
 
 
 
                                     CHAPTER 1
 
                                      Using XMT
 
 
 
          XMT is a standard MCR function, evoked by:
 
                MCR>XMT
 
          XMT prints the message:
 
          Terminal Transmission Program V3.3 
          Initializing operation using TT25:
 
          If TT25 is connected to a dial-up modem you must now dial the re-
          mote computer before continuing.  If the terminal is hardwired to
          the remote system, or when you have made the  connection  to  the
          remote via modem, XMT is ready for operation.
 
          XMT is now running with several defaults in effect:
 
               1.  ASCII transfer mode.
                   XMT expects files to be in ASCII format, (i.e.   source,
                   listings, etc.)
 
               2.  COPY mode is off.
                   When receiving a "file" from the remote terminal,  char-
                   acters typed at your terminal are not echoed to the out-
                   put file.
 
               3.  DELAY of 20 milliseconds.
                   XMT will wait 20 milliseconds after receiving a "prompt"
                   character   from   the   remote   terminal,  (usually  a
                   line-feed) before transmitting the next line of  a  file
                   to the remote computer.
 
               4.  ECHO Mode is off.
                   When file transfer is in process, all I/O is not printed
                   on  your  terminal.   A single flag character is printed
                   for each line transferred.
 
               5.  PROMPTED transmission is on.
                   XMT waits for a Line-Feed (or some other character)  be-
                   fore transmitting the next line of a file from the PDP11
                   to the remote computer.


          Using XMT                                                PAGE 1-2
                                                                  12-Jan-82
 
 
               6.  Several control characters are re-defined (see appendix)
                   Since ^C is used to inform XMT that you wish  to  change
                   some  operating  condition,  if you wish to send a ^C to
                   the remote computer, typing a ^B will cause a ^C  to  be
                   sent to the remote computer.  Note that although several
                   other re-defines are normally set, under IAS,  only  the
                   ^C re-define is necessary.
 
               7.  FULLDUPLEX mode is on
                   Characters typed at your terminal are not echoed  local-
                   ly, the remote computer must echo them.
 
               8.  8-BIT ASCII mode is off, no parity
                   Characters are transmitted with 7 data bits and the par-
                   ity bit off.
 
          These settings can be changed dynamically by the user  to  tailor
          XMT's characteristics to ease communication with other computers.
 
          This version of XMT  has  been  modified  for  IAS  (basically  a
          rewrite of the terminal I/O sections) by G.  Everhart.  In normal
          operation, it uses TT25 for connection to the "remote"  computer.
          TT25  should  normally be set up at system boot, but if necessary
          one may have to reset it to:
 
 
          MCR>SET /UIC=[1,1]            ;To change another Terminal setting
          MCR>TER TT25:/FULLDUPLEX      ;fix for no echo, full duplex I/O
          MCR>TER TT25:/BINARY          ;fix for no special ^C recognition
          MCR>TER TT25:/WIDTH:132       ;make width big enough
 
          This should allow the terminal  to  work  correctly.   Note  that
          you'll  have  to  try  various options when using it with non-DEC
          systems.  In its default state, it works well with other  IAS  or
          RSX11M  systems.   You  will  have to reset the characterstics of
          TT25 to permit someone to connect a terminal to it  and  have  it
          work  correctly.   Also,  by  the nature of the program, (it uses
          single-character QIO's for I/O to your terminal)  will  sometimes
          result in a noticable delay in output (or echo) at your terminal.
          However, it appears to work reliably  once  the  right  operating
          conditions and defaults are established.
 
          To leave XMT, type CTRL/C twice (CTRL/C is typed by holding  down
          the  CTRL  key  and  typing C), or by typing CTRL/C followed by X
          (eXit).


          
                                                                  12-Jan-82
 
 
 
 
 
 
 
 
 
                                     CHAPTER 2
 
                                     XMT Options
 
 
 
 
          To change any of the program settings/options, type  CTRL/C  fol-
          lowed  by  the upper case character signifying the setting/option
          desired.  Below is a table of options and their corresponding de-
          finitions:
 
 
                                        NOTE
 
              Do NOT type a carriage-return to enter or execute any  of
              these  commands.  Typing the single character of the com-
              mand is all that you need to execute that option.
 
 
               A - Changes the file transfer mode to ASCII if in the binary
                   mode, or changes the file transfer mode to binary if al-
                   ready in the ASCII mode.
 
               B - Sets the BREAK (logical spacing) key definition to  some
                   keyboard  character  which,  when  depressed,  creates a
                   'BREAK' condition to occur just like the 'BREAK' key  on
                   a teletype.
 
               C - Enter/exit Copy mode;  i.e., when receiving a file  from
                   the  remote  in  ASCII mode, all characters typed at the
                   keyboard are copied to the output file when also in Copy
                   mode.
 
               D - Set the length of delay that XMT should wait  after  re-
                   ceiving  a prompt character before sending the next line
                   of data from a disk file at the PDP11.   The  delay  can
                   range  from 0 to 99, where 0 corresponds to no delay and
                   99 corresponds to 99 clock ticks  (approximately  1  2/3
                   seconds).  If the length of the delay is a single digit,
                   typing a carriage-return after typing the digit will  be
                   sufficient  to  enter  the  delay.  You may also enter a
                   single digit for the delay by preceeding it with a zero.
                   You  cannot  enter a delay of more than two digits.  Any
                   characters entered other than 0 through 9 will cause the
                   default delay of 20 to be used and no error message will


          XMT Options                                              PAGE 2-2
                                                                  12-Jan-82
 
 
                   be given.
 
               E - Enter/exit Echo mode;  i.e., when receiving or transmit-
                   ting  a  file all input/output from/to the PDP11 disk is
                   printed on the user terminal.  This mode is useful  when
                   you wish to see the effects of transmission in progress.
                   In general, this mode should only be used when  you  are
                   logged  onto a high-speed terminal or when the amount of
                   printing is less than 2 full pages (at 1200 baud) or in-
                   definitely (at 300 baud or less).
 
               F - Receive a file From the remote.  A short status  of  the
                   applicable  options  in  effect is printed before a file
                   specification is requested.  The file  specification  is
                   29  or  fewer characters and follows the system standard
                   conventions for files.  Entering a name of less than  29
                   characters  requires  a carriage-return to enter the fi-
                   lename.  The RUBOUT or DELETE keys can be used  to  edit
                   out any errors made in typing the file spec.  Entry of a
                   null, or empty, filename will allow you to  exit  the  F
                   option  without  sending any data or creating any files.
                   Any previous execution of the F option that was not ter-
                   minated by either the O option or by exitting XMT is au-
                   tomatically terminated prior  to  the  printing  of  the
                   short options-in-effect summary.
 
               H - Prints a very brief Help summary of the purpose of  each
                   option.
 
               I - Terminates reading input from a PDP11 disk file if  such
                   a   file   transfer   was  taking  place.   The  message
                   "Transmission  Complete"  will  be  printed  if  a  file
                   transfer  is  terminated,  otherwise no action is taken.
                   This option is useful in aborting  the  transmission  of
                   data to the remote if problems in communication arise.
 
               O - The O option performs the same function for  terminating
                   a file receive operation (Output to the PDP11 disk) that
                   the I option performs on file transmit operations (Input
                   from  the  PDP11  disk).  This option is the only means,
                   other than by exitting XMT or by starting  another  file
                   receive  operation,  of  signalling the end of a receive
                   operation to XMT.  The message "Receive complete" prints
                   when a receive operation is terminated.
 
               P - Change transmit file mode from Prompted mode to  Prompt-
                   less,  and  vice-versa.  A message is printed indicating
                   which mode is in effect.  When changing to prompted mode
                   you  are  asked  which character sent by the remote com-
                   puter system should be used as the prompting  character.
                   Type the prompting character and XMT will, during a file
                   transmit operation, wait for this character  to  be  re-
                   ceived  from the remote computer before sending the next


          XMT Options                                              PAGE 2-3
                                                                  12-Jan-82
 
 
                   line of information to the remote.  Note that  XMT  will
                   send  the  first  line  of  input to the remote computer
                   without waiting for the prompt, but all other  lines  of
                   input  will wait for a prompt to be received before they
                   will be sent.
 
               R - Redefine/don't redefine control characters.  This option
                   enables  and disables the user-defined translation table
                   for control characters as described under  the  "^"  op-
                   tion.   A  message  is  printed which mode is in effect.
                   When in "Redefine mode" XMT will use a translation table
                   to convert any redefined control characters to some oth-
                   er control character so as to be able to "type" reserved
                   control  characters to the remote computer.  Examples of
                   reserved control characters are CTRL/C, CTRL/O,  CTRL/S,
                   CTRL/Q,  etc.  "Not redefined mode" disables this trans-
                   lation, but the translation table is not destroyed.
 
               S - Prints a Status of the options in effect for  XMT.   The
                   status  report  includes information about parity, ASCII
                   or binary modes, information about file transfer  opera-
                   tions, and prints the definition of the BREAK character,
                   if any.
 
               T - Starts a file Transmit operation.  This option  is  very
                   similar  to the F option except in the direction of data
                   transfer.  A check is made as to whether or not XMT  was
                   in the midst of a previously started file transmit oper-
                   ation, and if so, that transmit operation is terminated.
                   A  short  status  of  file transmit options-in-effect is
                   printed before you are requested to type in the name  of
                   the  file you wish to transfer to the remote system.  If
                   you just type  a  carriage-return,  XMT  simply  returns
                   without  initiating a file transfer.  Otherwise you must
                   enter a file name in the standard system format.  If the
                   name  of the file you enter does exist on disk a message
                   is printed indicating that the file is not found and  no
                   transfer  operation  is  initiated.   Otherwise  a  file
                   transfer is initiated which can be terminated by 1)  ex-
                   itting XMT, 2) using the I option, 3) using the T option
                   again and entering a carriage-return for the name, or by
                   4)  reaching  the  end  of  the input file.  The message
                   "Transmission complete" is printed when the transfer op-
                   eration is completed (or terminated).
 
               U - Unduplex or duplex the XMT program.  In  the  Unduplexed
                   mode  characters typed on the terminal are not echoed to
                   the terminal unless the  remote  computer  performs  the
                   echoing.  This mode is useful when communicating to com-
                   puter systems as other PDP11's.  For communication  with
                   systems  such  as TSO, however, the Duplexed mode is re-
                   quired if you wish to see the characters that you type.
 


          XMT Options                                              PAGE 2-4
                                                                  12-Jan-82
 
 
               X - EXit XMT.  All file transfers, if  any,  are  terminated
                   and control is returned to the RSX-11M Executive.
 
               8 - Enter 8-bit ASCII mode and exit 7-bit  ASCII,  or  leave
                   8-bit ASCII and enter 7-bit ASCII and be asked what par-
                   ity you desire.   This  mode  allows  you  to  determine
                   whether  or not the information you transmit and receive
                   will be full 8-bit ASCII or 7-bit  ASCII  with  software
                   generated  even, odd, mark, or no parity.  Some computer
                   systems require  specific  parity  settings,  but  other
                   PDP11's and TSO don't care.
 
               ^ - Allows you to redefine a control character as a  differ-
                   ent control character.  This allows you to use some oth-
                   erwise reserved control characters, such as CTRL/C,  and
                   allow you to send these characters to the remote system.
                   You will be asked to type  two  characters.   The  first
                   character  you  type will be the redefined character and
                   the second character you type will  be  the  definition.
                   To  enter  either of these characters may, and sometimes
                   must, enter the upper-case  equivalent  of  the  control
                   character.   The  characters  you type are automatically
                   converted to the  proper  control  character  and  their
                   upper-case  equivalent  is  printed  after  you type the
                   character.  For example, you wish to use  the  character
                   CTRL/W to signal when you transmit a CTRL/C.  Type the ^
                   option, the letter W, and the letter C and the redefini-
                   tion  has  been  set.  Assuming that XMT is in "Redefine
                   mode", every time you type a CTRL/W a CTRL/C is actually
                   sent  to the remote system.  If you wish to change a de-
                   finition, simply redefine it in the manner given above.
 


          
                                                                  12-Jan-82
 
 
 
 
 
 
 
 
 
                                     CHAPTER 3
 
                               Summary of Capabilities
 
 
 
 
               1.  Full or half duplex operation
 
               2.  Disk file transmit and receive
 
               3.  Prompt character checking and delay
 
               4.  Optional echoing of files during transmission and recep-
                   tion
 
               5.  A short help message summary
 
               6.  The ability to transmit  a  file  while  also  receiving
                   another file
 
               7.  The ability to transfer files using a full 8 bits
 
               8.  The capability of transferring  files  with  or  without
                   prompted handshaking
 
               9.  The option of preventing everything entered at the  user
                   terminal from being copied to an output disk file during
                   a receive operation
 
               10. The ability to create a  'BREAK',  or  logical  spacing,
                   condition  so  as to be able to interrupt remote devices
                   such as TSO
 
               11. The capability of defining almost any keyboard character
                   to be used to signal when a BREAK was desired
 
               12. The ability to perform  translations  of  control  char-
                   acters  entered  at  the user terminal to characters not
                   normally able to  be  entered  without  interception  by
                   RSX-11M
 
               13. The ability to turn on and  off  the  control  character
                   translation without losing the previous definitions
 
               14. The inclusion of a "status" subroutine which enables the


          Summary of Capabilities                                  PAGE 3-2
                                                                  12-Jan-82
 
 
                   user  to see what parameters are currently in effect for
                   the program
 
               15. The ability to set the mode of parity (even, odd,  mark,
                   or  none) to be used when transmitting each character to
                   the remote while the 7-bit character mode is in effect.
 


          
                                                                  12-Jan-82
 
 
 
 
 
 
 
 
 
                                     APPENDIX A
 
                      XMT Default Control Character Definitions
 
 
 
                      Typed Character   Resulting Character
 
                          ctrl/A             ctrl/S
                          ctrl/B             ctrl/C
                          ctrl/P             ctrl/O
                          ctrl/W             ctrl/Q
                          ctrl/X             ctrl/Z
 
 
                                List of XMT commands
 
                A - Change file transfer mode (Binary/Ascii)
                B - Set BREAK character
                C - Enter/exit copy mode
                D - Set length of delay (in ticks)
                E - Enter/exit echo mode
                F - Recieve File from remote computer
                H - Prints HELP summary
                I - Terminate transmission to remote computer
                O - Terminate reception from remote computer
                P - Enter/exit Prompted transmission mode
                R - Redefine/don't redefine control chararacter mode
                S - Print current program status
                T - Transmit file to remote computer
                U - Enter/exit full duplex mode
                X - Exit XMT
                8 - Enter/exit 8-bit ASCII mode
                ^ - Redefine control character