SSTs and Fortran
			---- --- -------



	Author: Richard Neitzel
		Process Control Applications
		312 Laveta Pass
		Golden, CO 80401

		13-Apr-87






	Programs sometimes go bump in the night and exit due some 
nastiness, such as memory protection violations, odd addresses, etc. 
Since the only notification of this behavior is given to the invoking 
terminal, it is easy to not have any idea what happened, especially in 
a production enviroment where the answer is run it again or reboot. We 
have a large number of process control stations running in this 
manner. Since we have redirected the console logger to a file via COT, 
we wished to have termination notice given on the log. 

	The two code sections SST and F77SST do just this. SST is written 
in Macro-11 to use the sstvec$ directive to remap the vector for the 
following ssts: 
  odd address, memory protection violation, t bit trap, iot trap, 
reserved instruction and non-RSX emt. 

	The F77 file F77SST contains a subroutine that of itself does 
nothing. Instead there are entry points that correspond to the names 
given the new sst vectors. When an sst occurs the code at that entry 
point is executed. The code supplied does the following: get the task 
name, put it in the correct message, set up a qio with write break 
through, issue the qio to invoking terminal and console, then exit. 
The qio can be a standard non-break through if desired, since to use 
io.wbt requires that the task be built using /PR:0. 

	It is also possible to simply continue program execution if 
desired. In this case a simple return from interrupt is used, for 
example on an BPT:
		bpt::	rti   OR   bpt::	qio$ (msg)
						rti
Obviously since you need to use the rti instruction, this can only be 
done from Macro.

	It is likely that a real RSX wizard can take this one step 
further and give back the approximate line of the problem, but that is 
currently beyond my expertise. If someone does this, please contact 
me:

		Richard Neitzel
		312 Laveta Pass
		Golden, CO
		80401

		303 - 966 - 7203 or 303 - 279 - 1935