BATCH - Batch Processing for RSX-11M
		====================================

			User Guide
			==========

 As  RSX-11M  does not (yet) support batch processing, a small version
 of  it  has  been developed using the virtual terminal driver (VTDRV)
 developed  by  Dave  Elderkin. The main purpose of BATCH is simply to
 run  an  indirect  command  file  without  tying  up  a terminal, and
 creating  a  log  file  of  the  output.  It  also has a facility for
 supplying data 'inline' to a program.

 Before BATCH processing can be initiated, the virtual terminal driver
 must  be loaded, and the tasks BATCH.TSK and SUB.TSK installed. Files
 are then  submitted to the processor via a command of the form:-

	SUBMIT	logon-text	<$>filename

 where:- logon-text  is  any  valid  command-line to HELLO, containing
                account and password.
         $      is  specified  if  the file to be processed is a BATCH
                data (see later)
         filename  is  the  name  of  the  command  or  data file to be
                processed.  The extension must be omitted and defaults
                to  .CMD  for  command files, and .DAT for data files.
                The  filename  may  be  up  to  9  characters long for
                command files, or 6 for data files.

 Examples:-
		SUB	1/10/FRED	BUILD
		SUB	PHIL/		$XDAT

 The  command (or data) files must reside under the user's current UIC
 (irrespective  of the account he specifies on the SUBMIT line) and on
 his  current system disk.  BATCH will create an output log file (with
 the  same  name as the input file but with an extension of .LOG and a
 version  number  of  1)  on  the same disk/UIC.  Note that in certain
 cases  the  output  log  file will be in a slightly odd format which,
 while  it  will  print successfully on the terminal or printer, could
 cause odd results if edited by any editor other than TECO.



 The  'data files' mentioned above (and characterised by a leading '$'
 sign in the SUBMIT line) are files containing instructions/data to be
 processed  by  the  Batch  Processor  itself.    These files may only
 contain lines in one of two forms:-

    MCR commands - These  are passed to the Virtual Terminal Driver in
                   the form required by MCR
    Data Lines   -  These are identified by a leading ! and are passed
                    (minus  the  !)  to the Virtual Terminal Driver in
                    the form required by most utility programs. If the
                    first  character  after  the  ! is a ^ it, too, is
                    omitted  and  the next character is interpreted as
                    the corresponding control character.

 For example, a data file containing:-

	PIP
	!/LI
	!^Z

 would produce a PIP listing in the log file.

 There  is  also  a  small program, called BTQ, which will display the
 current contents of the batch queue (not including the file currently
 being  processed). It is run without arguments and produces a list of
 the form:-

 BATCH WAIT QUEUE
 PHIL/         	 ZZZ      	TT1:
 1/10/SYS      	$DAT      	TT5:
 FRED/FRED     	 BUILD    	TT3:


 A  measure  of  security is supplied in that if a non-privileged user
 runs  the program, then all of the logon-text after the second / will
 be suppressed - i.e. if the second format above was used the password
 would not be printed for a non-privileged user.




 The following error messages may be output from the BATCH system:

 1.  SUB -- COMMAND SYNTAX ERROR

     You made a mistake in your submit line.  Try again.

 2.  SUB -- SEND DATA OR REQUEST ERROR

     The  SUBMIT  task could not communicate with the BATCH processor.
     Probably  it  is  either  not installed or has the wrong taskname
     (should be BAT...).

 3.  BAT -- I/O ERROR ON XXX FILE

     An  I/O  error  occurred on one of the files BATCH accesses (CMD,
     DAT or LOG).  Check to see that your input files are readable and
     that there is enough space on the disk for your LOG file.

 4.  BAT -- ATTACH FAILURE ON VIRTUAL TERMINAL

     BATCH  could  not  attach to the virtual terminal VT1:.  The most
     likely  reason is that the Virtual Terminal Driver is not loaded.
     load it and try again.

 5.  BAT -- USER CANNOT LOG ONTO VT, TRY AGAIN

     BATCH  could  not  log on to the virtual terminal using the login
     text you gave it.  Probably you typed part of it incorrectly - if
     so, correct it and try again.

 6.  BTQ -- BATCH PROCESSOR NOT INSTALLED

     BTQ  cannot  list  out  the  Batch Queue as the BATCH task is not
     installed.   If you wish to do any batch processing install BATCH
     first.

 7.  BTQ -- OPEN FAILURE ON RSX11M.STB

     Because  of  the  way  BTQ  works,  the pseudo-device LB: must be
     pointing  to  a  disk holding the RSX11M.STB file (in [1,54]) for
     the  current  system.    If this message occurs it probably means
     that LB: is not correctly set - adjust it and try again.

 8.  BTQ -- SYMBOL NOT FOUND IN RSX11M.STB

     If  this  message  ever  occurs then you have something seriously
     wrong  with  your  RSX11M.STB  file.   I wouldn't go much further
     without carefully checking it.




		BATCH - Batch Processing for RSX-11M
		====================================

			System Guide
			============

 BATCH  is  a  simple attempt to provide batch processing for RSX-11M.
 In  this context Batch Processing is interpreted as implying:-

	1) No terminal is tied up during processing
	2) A log of the run is available afterwards
	3) Single-streaming of jobs will be provided


 A  facility has also been added whereby input data can be supplied to
 programs that prompt for it.  The intention of this was to facilitate
 the running of benchmarks, but there has not yet been time to see how
 successfully it does so.

 As  it  seems  very likely that RSX-11M will officially support Batch
 Processing  before  long (as it is available on RSX-11M-PLUS) no real
 attempt  has  been made to make this into a full 'bells-and-whistles'
 product.   Rather it is intended merely to be a useful adjunct to the
 system.

 The original code was written by Eric Rosdol in SWS in Vienna and was
 published  in  the  Software Dispatch in 1978.  Several modifications
 were  then  made  to  it by James Downward, who also placed it in the
 DECUS    Library.     This  version  was  further  modified  by  Phil
 Stephensen-Payne as described in the code.

 The  programs  also require the use of the Virtual Terminal Driver as
 originally designed by Dave Elderkin in 1977.  Minor chages have been
 made to it by Phil Stephensen-Payne for it to run on RSX-11M V3.2 and
 to  support this version of BATCH.  Again no attempt has been made to
 turn  this  into  a  polished product as it seems likely that virtual
 terminals will be supported by RSX-11M in the near future.

 The following sections of this document contain brief discussions and
 comments  on  the various elements of the BATCH system.  The code is,
 however,  pretty  well  commented  and should be used as the ultimate
 reference source if any modifications are to be made.



1.	SUB - Program to submit a Batch Request
	=======================================

 SUB  is  the  program  responsible for submitting a request to BATCH.
 This is a major area in which this BATCH cannot really perform like a
 proper BATCH.  In the latter the user need only supply a filename and
 the job will be run with his UIC and privileges automatically.  BATCH
 does  not really have this option as the Virtual Terminal driver must
 (currently at least) be treated like an ordinary terminal.

 There are a number of ways of coping with this, i.e.
	1) Keep the VT terminal always logged in & just change UIC
	2) Modify the VT driver to allow BATCH to force its default UIC
	   & privileges
	3) Force the user to specify an account/password each time

 Method  1) would allow any user access to all accounts, and method 2)
 would  be  difficult  to  implement  without  similar problems.  Thus
 (taking the easy way out) method 3) has been used.

 The basic format of the Submit command line is therefore:-

	SUB logintext filename

 where 'logintext' is any valid account/password combination for HELLO
 (e.g.  1/2/FRED or FRED/FRED) and filename is the name of the file to
 be   executed.    This  file  is  assumed  to  live,  not  under  the
 account/system  disk  corresponding  to the login text, but under the
 account/system  disk  the  user is currently set to.  This is because
 RSX-11M users often have one account they log in under, but then work
 in  several  accounts,  just  resetting  their  UIC.  By adopting the
 method  just described they can then use batch files from any account
 without  having  to set up an account entry for each one.  (For those
 users  who  do  stick  to the account they log in under, this will of
 course make no difference.)

 In  general  'filename'  is  a  9-character filename representing the
 command  file to be executed (it will be given an extension of .CMD).
 For  data  files,  however  (i.e. ones containing embedded data to be
 passed  directly  to a prompting task) the filename must be at most 6
 characters  long  and  preceded  by a '$'.  Ones of this type will be
 given an extension of .DAT.

 SUB  first  parses  the  command-line  it  is given.  It assumes that
 everything  from  the  first  non-blank character, to the first space
 after  that  is the text for HELLO, and the only requirements imposed
 on that text are that it should contain at least one slash (/) and at
 most  two.    It  then  assumes that everything from there to the end
 comprise  the  filename,  and  checks to make sure this contains only
 valid  RAD50  characters.    SUB  then  sets  up  a  13-word  RSX-11M
 Send/Receive packet as follows:-

	Words 1 to 7	- Login text (unchanged)
	Words 8 to 10	- Filename (in RAD50)
	Word 11		- User's TI: device (special format)
	Word 12		- User's SY: device (special format)
	Word 13		- User's UIC (2 octal bytes)



 If  the  filename  was  specified  with  a  leading  '$' then that is
 stripped  off,  the filename is put in Words 8 & 9 and Word 10 is set
 to  -1  (not a valid RAD50 combination).  The 'special format' of the
 TI:  and  SY:  devices  consists  of  the  two-character  ASCII  code
 translated  as  RAD50  plus  the  unti  number  in binary - this will
 adequately  cope  with units up to 50 (octal) which should be enough.
 The TI: device is required by Batch for completion reporting, and the
 SY:/UIC  are  needed  to  find the input file and to place the output
 (.LOG) file.

 Having built the packet, SUB then sends it to BATCH and request BATCH
 (in case it is not running).  SUB then exits.

 SUB  is  built  by  the command file SUB.CMD.  It is a non-privileged
 task, with only 1 unit and a taskname of ...SUB.



2.	BATCH - Program to process Batch Requests
	=========================================

 BATCH is the main program that actually processes the batch requests.
 It   is  basically  very  simple  and  the  major  complications  are
 introduced  by  the  different ways in which various MCR tasks react.
 The major problems are:-

        1) Most  tasks, when terminating, output a '>' sign, which can
           be  picked  up  by  BATCH, but some (e.g. BYE) do not and a
           timeout  must be put on every read to the VT driver to cope
           with  this. (Note that the driver could be modified to time
           out such reads automatically, but I was reluctant to change
           the driver more than I had to.)
        2) HELLO  and  AT.,  if  they  hit  an error, do not terminate
           normally,  and  so it is necessary to check for their error
           messages   as  alternate  termination  possibilities.    In
           addition AT. uses the same format for its error messages as
           for its informational messages and while none of the latter
           should  occur it was felt that a check should be put in for
           the  DELAYING/CONTINUING combination (output in response to
           a  .DELAY)  as, should a user include them in his file, the
           reason for the file terminating is not at all obvious.
        3) Tasks  that  prompt  for  input  require a different format
           input  line to MCR.  It would appear that every line passed
           to MCR must have a trailing carriage-return, and every line
           passed  to  a  prompting  task  must  not  have  a trailing
           carriage    return.    Hence  special  code  is  needed  to
           distinguish the two cases.
        4) Tasks  which  output a lot of information to the 'terminal'
           appear  to  send out 80 bytes chunks with embedded carriage
           return.    This works fine when it appears on the terminal,
           but looks a bit strange in a file.  The method adopted sets
           up  the  file  so  that  it  will  print  on a terminal (or
           printer) as the original utility would - but any attempt to
           edit the output file (unless you use TECO) can produce some
           very  odd results.  [I'm not sure whether this situation is
           caused by the utilities, MCR or the VT driver.]
        5) For  the  VT  driver to succeed, the virtual terminals must
           pretend  that  they  are  terminals  (or  MCR will get very
           upset).    Because  of  this,  if  the system is built with
           'Checkpoint during Terminal Input' support, the system will
           try  and  checkpoint  BATCH  during  VT  I/O  if it is made
           checkpointable  -  and,  of course, the poor VT driver does
           not have the code to cope with it.  BATCH must therefore be
           made non-checkpointable for the duration of all such I/O.

 Bearing  the above in mind, the processing of BATCH is fairly simple.
 It  dequeues  a  request from its receive queue (exiting if there are
 none)  and  sets itself to the UIC specified and assigns units to the
 given  SY:  and  TI:  devices.  It then opens the output file and, if
 processing a 'data file', the input file.  It attempts to log off the
 virtual  terminal (in case it was already logged on) and to log it on
 with  the  login text supplied.  If that succeeds it sets the virtual
 terminal  to  the  user's  account  and writes the headers to the log
 file,  and  calls  ATPRC or BATPRC to process 'AT. command files' and
 'data files' respectively. When they complete it logs out the virtual
 terminal and closes and truncates the log file and looks for the next
 request.



 ATPRC merely sends the line '@filename' to the Virtual Terminal, logs
 any  output it gets, and waits for either an '@<EOF>' or an AT. error
 message to be logged, at which point it terminates.

 BATPRC  basically reads the input file a line at a time, passing each
 one   to  the  virtual  terminal,  logging  it  and  any  reply,  and
 terminating  when  the  input  file  is  finished.   'Data lines' are
 flagging  by  a  preceding  '!'  and these are passed to the terminal
 without  the  leading  '!'  and  as 'solicited writes' (see the VTDRV
 writeup  later).    In addition if the first character of a data line
 (after  the !) is a '^' then it too is omitted and the next character
 is  interpreted  as a control character (so that the user may include
 ^Z in his file).  Each line is considered 'acted upon' if the read to
 the  VT  driver  either  times out, is rejected with an IE.EOF (which
 often  means  the  other  unit  is  trying  to  read)  or if the last
 character of the input buffer is a '>' - this should be borne in mind
 if this facility is used with user programs.

 BATCH  is assembled and built with the command file BATCH.CMD.  It is
 a  privileged,  slave  task (/PR:0/SL) which references EXEMC.MLB and
 RSXMC.MAC.    It  has  a taskname of BAT... and should really have an
 'above-average' priority (e.g. 65).



3.	BTQ - Batch Queue Lister
	========================

 BTQ  is  a  small  task  that  will list out the current Batch Queue.
 Unlike  most  'professional'  Batch  Queue Listers it cannot list the
 name  of the job currently being run - this would require some rather
 hairy  code.    BTQ works on the standard principle of switching into
 system state, finding the TCB of BAT... and hence tracing its Receive
 Queue.    Note that BTQ uses the 'RSX11M.STB Lookup' method described
 in the writeup of BOILER.MAC.

 BTQ  simply  copies the Receive Queue for BAT... into its own buffer,
 and  then  outputs a line for each entry, listing the login text, the
 filename  and  the  originating  terminal.    An  attempt  is made at
 security  for  the  program checks to see if the person who requested
 the  listing  is  privileged, and if not only lists the login text as
 far  as  the  second  slash  (/).   This will only work if the submit
 request  used  the full HELLO format (e.g. 1/2/FRED) but as I have no
 concern about security on my system I did not bother to improve on it
 (i.e.  only listing up to the last slash specified) - that is left as
 a user exercise.

 BTQ is assembled and built by BTQ.CMD.  It is a privileged task (/PR)
 and  references  EXEMC.MLB and RSXMC.MAC.  It uses only two units and
 should have a task-name of ...BTQ.



4.	VTDRV - The Virtual Terminal Driver
	===================================

 The Virtual Terminal Driver is an essential part of the BATCH system.
 Basically  the  driver  is  very  simple  in that it sets up the data
 structures  (in  VTTAB) for two terminals known as VT0: and VT1:.  If
 the user sends a Write request to VT1: then the driver will use it as
 a  reply  to  a  read  from VT0:, or will (usually) pass it to MCR as
 'unsolicited  input'  from VT0:.  Conversely, if the user does a read
 to VT1: then the driver will satisfy it the next time somebody does a
 write to unit VT0:.

 Because of the tendency of the system to crash when you start playing
 with  user-written  drivers,  not  a lot of work has been done on the
 Virtual  Terminal  Driver  to  see  how it could be improved, or what
 would  happen  if various things were changed.  For instance it would
 seem    feasible    to    use  this  for  communicating  between  two
 non-privileged  tasks  (one  reading/writing to VT0: and one to VT1:)
 but I don't guarantee it would work, and have not tried it.  It would
 also be nice if the UCBs could be simplified but, because of the need
 for  the  virtual  terminals  to  look  to  the  system like ordinary
 terminals, this is no easy job and has not been attempted.

 For  more  information  on the driver the (brave) user is referred to
 the  source  code  itself.    The  only changes I have made from Dave
 Elderkin's original design are:-
        1) Updated the UCBs in line with RSX-11M V3.2 changes.
        2) Added a 'Solicited Write' feature to the interface to VT1:.
           A  'Solicited Write' to VT1: will never be passed to MCR as
           unsolicited  input but will instead be held until a read is
           issued  to  VT0:.  This was implemented for the 'data file'
           aspect  of BATCH as otherwise the prompting task could miss
           the  data  because it wasn't fast enough. Note that as this
           request  will  hang forever if no read request is issued to
           VT0: it should probably be timed out.
        3) A  problem with the original VT driver came if you tried to
           abort  a  task  running  'from'  VT0:.  First TKTN tried to
           output  an  'exit'  message  to  VT0: and then MCR tried to
           output  a '>'.  As there was no soliciting task, the driver
           ignored  them  both  and  both TKTN and MCR hung the system
           timing  them  out (a total of about 15 seconds in which the
           system  hung  completely).  The driver has been modified to
           terminate  immediately  any unsolicited writes from TKTN or
           MCR.

 The  Virtual terminal driver is built with VTDRV.CMD in the usual way
 for a Loadable Driver.