Terminal Security System 
                              Product Description








                               Cargill Grain Lab
                                 Randy Baldwin
                               November 7, 1985
                            SM:[1,100]SCLIBRIEF.DOC

         SCLI Overview                                         Page 2
         



         1.  Introduction

              This document provides a brief product  description  of
         the  security CLI - SCLI.  It contains a description of what
         SCLI provides, how it is implemented and maintainance proce-
         dures.



         1.1  SCLI Overview

              SCLI is a user-written command line interpreter,  which
         provides  additional access protection to one or more serial
         ports, beyond that provided by the RSX login procedure.  The
         secure system consists of three 'components':  the SCLI task
         itself, a modified RSX BYE program, and a patch to  the  RSX
         TT  driver.   This system has been designed to operate fully
         un-attended.  It will be run at system  startup,  and  never
         shut  down.  In fact, the system is very difficult to elimi-
         nate.  

              SCLI implements access protection by simply sitting  on
         the  terminal(s), absorbing all input.  When SCLI receives a
         valid password on a protected terminal, it gives control  of
         the  terminal to MCR, and remains 'quiet' until the terminal
         is logged off.  At that point, BYE  gives  control  back  to
         SCLI, re-establishing protection.  

              When SCLI is first  started,  normally  just  following
         system  boot,  it  takes control of the protected terminals.
         As long as SCLI remains  active  (normally  'forever'),  the
         protected  terminals are in one of three states:  protected,
         logged on, or disabled.  A terminal is protected  when  SCLI
         is  that  terminal's  CLI.  A logged on terminal has already
         been 'admitted' to the system, and is  in  use  by  a  valid
         user.   A terminal can become disabled in the unlikely event
         that SCLI is shut down.  In this state, no CLI is  connected
         to  the  terminal,  and it is effectively slaved.  Note that
         this state occurs briefly during  system  shutdown,  between
         the  time  that  SHUTUP  disables the CLI, and the time that
         shutdown completes.

              SCLI places terminals which it is protecting in one  of
         two  internal  states:   normal, and mumble mode.  In normal
         mode, SCLI will accept a valid password, and give  the  user
         access  to  the  system.   In mumble mode, SCLI has detected
         unauthorized attempts to access the  system;  all  input  is
         treated as invalid, and the user will 'never' gain access to
         the system.  


         SCLI Overview                                         Page 3
         



              Mumble mode is triggered by a preset number of  sequen-
         tial  invalid login attempts.  Once in mumble mode, the (po-
         tential) user must wait a preset time interval before  again
         attempting  to  log  in.  If the timer expires, and no input
         has been received, SCLI assumes that the villian  has  left,
         and  a  new user is attempting to gain access.  On the other
         hand, if the user keeps  trying,  SCLI  simply  re-sets  the
         timer, perpetuating mumble mode.  

              SCLI maintains a log of all activity on both  the  Con-
         sole  (CO:  or COT), and the system error log file.  The log
         to CO:  is more detailed, since it is assumed that the  con-
         sole  log  will be purged more frequently than the error log
         file.  

              SCLI is also sensitive to messages issued via  the  MCR
         CLI  commands.  There are currently three messages:  two en-
         able/disable dumping of all invalid  input  to  the  console
         file.  These are used for observing activity during attempt-
         ed break-ins to the system.  The third message provides  the
         only  known  means  of  shutting SCLI down while keeping the
         system running.  



         1.2  SCLI Implementation.

              This chapter describes the process required  to  imple-
         ment SCLI on a operating RSX system.



         1.2.1  Programs and System modifications.  --

              The SCLI product consists of  three  related  programs.
         One,  SCLI,  is a user written program and the other two are
         RSX11M (DEC) supplied programs that are modified to fit with
         SCLI.



         1.2.1.1  SCLI program --

              The SCLI program must be  rebuilt  and  configured  for
         each  site.   The reason for this is each site (usually) has
         differant needs for secure terminals.  (i.e.  all modems are
         not on the same port).  Also passwords and user messages are
         unique for each installation.

              Password modifications is is accomplished by rebuilding
         several  modules of the SCLI program thus user password mod-

         SCLI Overview                                         Page 4
         



         ification is not possible.  This is also an  added  security
         benefit as it places control over the passwords.



         1.2.1.2  BYE program modifications.  --

              The modifications to BYE, RSX's log  off  program,  are
         required  to  inform BYE which terminals are to be protected
         and thus connected to SCLI when they  are  logged  off.   If
         terminals  are to be added or removed from the security pro-
         gram BYE will have to be modified to reflect these  changes.
         (This  may  not require rebuilding as it may be done on-site
         via ZAP depending upon the situation).



         1.2.1.3  TTDRV program modifications.  --

              The modifications to TTDRV, RSX's terminal driver  pro-
         gram,  are required to prevent TTDRV from automatically set-
         ting a remote (modem) port's CLI to MCR when it is answered.
         This  mod  may be done by rebuilding the TTDRV program or by
         using ZAP or OPEN/SAVE to alter the tasks code.  This  is  a
         one  time modification that must be done and is not affected
         by adding or subtracting terminals from SCLI or by  password
         modification.



         1.3  Related Documents

              There are several documents available to further expla-
         in and aid in the configuration and modification of the SCLI
         product.  These documents are available upon request and are
         listed below.

              o  SCLIMAN.DOC -- This is the technical support  manual
                 for  SCLI.   It  contains  module design information
                 along with overall  design  guidelines.   Additional
                 information  is  provided for the use of maintainers
                 of the program, including instructions for modifying
                 passwords,  response lines, protected terminals, and
                 so on.  A chapter describing  modifications  to  the
                 RSX  system  required  by the security system is in-
                 cluded, along with instructions for  installing  the
                 changes.  

              o  SCLIREV.DOC -- This document summarizes design  fea-
                 tures of the dial-in security project.  


         SCLI Overview                                         Page 5
         



              o  SCLISUG.DOC -- This document presents user's  infor-
                 mation  for  the terminal security system.  Included
                 in this document are descriptions of the normal  op-
                 eration of the secure system, including instructions
                 for obtaining reports of SCLI  activity.   Also  in-
                 cluded  are  descriptions of the various log entries
                 and error messages produced by SCLI.  


         
         





                                   CONTENTS



         1.  Introduction . . . . . . . . . . . . . . . . . . . . . 2
             1.1  SCLI Overview . . . . . . . . . . . . . . . . . . 2
             1.2  SCLI Implementation.  . . . . . . . . . . . . . . 3
                  1.2.1  Programs and System modifications. . . . . 3
                         1.2.1.1  SCLI program  . . . . . . . . . . 3
                         1.2.1.2  BYE program modifications.  . . . 4
                         1.2.1.3  TTDRV program modifications.  . . 4
             1.3  Related Documents . . . . . . . . . . . . . . . . 4