Terminal Security System
                               Technical Manual




                                 Prepared for 
                               Cargill Grain Lab
                            Minneapolis, Minnesota




                                      by




                               Cargill Grain Lab
                            Computer Systems Group
                                 Jim Bostwick
                                 June 20, 1985
                            Sy42:[1,100]SCLIMAN.DOC

         
         





                                  CHAPTER 1

                                 Introduction



              This is the technical support manual for  the  security
         CLI  -  SCLI.   It  contains module design information along
         with overall design guidelines.  Additional  information  is
         provided  for the use of maintainers of the program, includ-
         ing instructions for modifying  passwords,  response  lines,
         protected terminals, and so on.  A chapter describing modif-
         ications to the RSX system required by the  security  system
         is  included,  along  with  instructions  for installing the
         changes.  



         1.1  Overview

              SCLI is a user-written command line interpreter,  which
         provides  additional access protection to one or more serial
         ports, beyond that provided by the RSX login procedure.  The
         secure system consists of three 'components':  the SCLI task
         itself, a modified RSX BYE program, and a patch to  the  RSX
         TT driver.  

              The BYE modification causes BYE to determine if a  pro-
         tected  terminal  is being logged off.  If this is the case,
         BYE resets the CLI for that terminal to SCLI.  

              The terminal driver patch prevents the driver from  ar-
         bitrarily  and  unconditionally setting a remote port to MCR
         when the modem is answered.  This is a two-line  patch,  and
         may be implemented using ZAP or OPEN/SAVE.

              These two modifications set up a  situation  where  any
         protected  port  which  is  not currently logged on is under
         control of SCLI.  SCLI then obtains all input  to  the  pro-
         tected  port.   SCLI responds to the proper input by setting
         the port to MCR CLI, allowing the user to log on and use the
         system normally.  

              This system has been  designed  to  operate  fully  un-
         attended.   It will be run at system startup, and never shut
         down.  In fact, the system is very difficult to eliminate.  

         
         





                                  CHAPTER 2

                                SCLI Narrative



              SCLI is a non-priveleged task.  However, when installed
         as  a  CLI, SCLI takes on several normally priveleged attri-
         butes.  SCLI implements access protection by simply  sitting
         on the terminal(s), absorbing all input.  When SCLI receives
         a valid password on a protected terminal, it  gives  control
         of the terminal to MCR, and remains 'quiet' until the termi-
         nal is logged off.  At that point, BYE gives control back to
         SCLI, re-establishing protection.  

              When SCLI is first  started,  normally  just  following
         system  boot,  it  takes control of the protected terminals.
         As long as SCLI remains  active  (normally  'forever'),  the
         protected  terminals are in one of three states:  protected,
         logged on, or disabled.  A terminal is protected  when  SCLI
         is  that  terminal's  CLI.  A logged on terminal has already
         been 'admitted' to the system, and is  in  use  by  a  valid
         user.   A terminal can become disabled in the unlikely event
         that SCLI is shut down.  In this state, no CLI is  connected
         to  the  terminal,  and it is effectively slaved.  Note that
         this state occurs briefly during  system  shutdown,  between
         the  time  that  SHUTUP  disables the CLI, and the time that
         shutdown completes.

              SCLI places terminals which it is protecting in one  of
         two  internal  states:   normal, and mumble mode.  In normal
         mode, SCLI will accept a valid password, and give  the  user
         access  to  the  system.   In mumble mode, SCLI has detected
         unauthorized attempts to access the  system;  all  input  is
         treated as invalid, and the user will 'never' gain access to
         the system.  

              Mumble mode is triggered by a preset number of  sequen-
         tial  invalid login attempts.  Once in mumble mode, the (po-
         tential) user must wait a preset time interval before  again
         attempting  to  log  in.  If the timer expires, and no input
         has been received, SCLI assumes that the villian  has  left,
         and  a  new user is attempting to gain access.  On the other
         hand, if the user keeps  trying,  SCLI  simply  re-sets  the
         timer, perpetuating mumble mode.  

              SCLI maintains a log of all activity on both  the  Con-
         sole  (CO:  or COT), and the system error log file.  The log
         to CO:  is more detailed, since it is assumed that the  con-

         SCLI Narrative                                      Page 2-2
         



         sole  log  will be purged more frequently than the error log
         file.  

              SCLI is also sensitive to messages issued via  the  MCR
         CLI  commands.  There are currently three messages:  two en-
         able/disable dumping of all invalid  input  to  the  console
         file.  These are used for observing activity during attempt-
         ed break-ins to the system.  The third message provides  the
         only  known  means  of  shutting SCLI down while keeping the
         system running.  


                                     NOTE

              This third message is known to a  few  programmers
              at  the Grain Lab only.  It is not to be made ava-
              ilable to Grain Lab staff in general, nor to plant
              staff  under  any circumstances.  Should it be re-
              quired to provide plant staff with a shutdown  me-
              chanism,  another  message  should  be defined for
              thier use.  



         2.1  SCLI Walkthru

              This section comprises a brief walkthrough of the  SCLI
         task itself.  Details of individual module action are conta-
         inied in subsequent chapters.  

              SCLI is normally in a stopped state.  Initialization is
         only  performed  at  system  startup, or following a program
         crash.  Note that the RSX executive will  automatically  re-
         start  SCLI as needed, so that the only truly fatal error is
         one which continually crashes SCLI.  

              Initialization is brief, consiting of assigning  a  LUN
         (2)  to  the  CO:  device, and clearing out the user-id, and
         invalid counts for each protected terminal.  

              Following initialization, SCLI lives in  a  loop  which
         obtains  a  'command'  from  the system (RSX), processes it,
         then loops.  The executive will STOP SCLI until a command is
         available.  

              Commands take two forms:   user  input,  and  messages.
         User  input  comes  from  one  of  the  protected terminals.
         Messages come from the  system,  either  automatically  when
         events  affecting SCLI occur, or in response to the MCR "CLI
         /MES" command.  


         SCLI Narrative                                      Page 2-3
         



              The main code immediately determines if  the  'command'
         is  user input or a message.  All message processing is done
         in subroutine DOMSG.  User input is processed  in  the  main
         SCLI module.  

              All input is encrypted.  The  encrypted  text  is  then
         compared  against a command table, containing pre-encrypted,
         known commands.  



         2.1.1  Command Input 

              Input commands are matched against the  command  table.
         The  issuing  tt  is  also  determined and the corresponding
         entry in the tt-table is located.  If no entry  exists,  the
         command is ignored (a log entry is made, however).  Assuming
         the command comes from a known tt, the action taken  depends
         upon  two  things:   1)  the action specified in the command
         table (pass/fail); and 2) the current mumble status  of  the
         terminal.  

              If the terminal is in mumble-mode, all  input  commands
         are treated alike:  a 'random' reply is issued to the termi-
         nal, and the foo-count is incremented.  If the  terminal  is
         not in mumble mode, commands with the ac.pas attribute cause
         SCLI to admit the user.  Commands with  the  fail  attribute
         (ac.fai), or those not found in the command table, cause the
         foo-count to be incremented, and the reply message from  the
         table  issued  to the terminal.  If, after incrementing, the
         foo count exceeds the pre-defined MAXFOO, MBLON is called to
         place the terminal in mumble mode.  

              SCLI admits a user to the system by first clearing  the
         foo-count,  and  total-foo,  saving  the  user-id in the tt-
         table, marking the terminal as 'logged on',  and  issuing  a
         SCLI$  directive to set the terminal to MCR.  This gives the
         user access to the standard RSX login procedures.  



         2.1.2  Mumble Processing

              Mumble mode simply means that no input from the  termi-
         nal  will  be  accepted as a valid password.  Mumble mode is
         triggered by a number of invalid commands which exceeds  the
         MAXFOO limit.  It is terminated by a timer.  Once in mumble-
         mode, any command input causes mumble mode to be  perpetuat-
         ed.   Only  if  the  terminal  is 'quiet' (e.g., no commands
         received by SCLI from that  terminal)  for  a  predetermined
         time  will  mumble mode be reset.  This is handled in module

         SCLI Narrative                                      Page 2-4
         



         MUMBLE, which contains  the  MBLON  initiator  routine,  and
         MBLAST, the timer service routine.  

              When mumble mode is entered, a timer is  started,  with
         MBLAST specified as the entry point.  Since several terminal
         may be in mumble mode at one time, the terminal  is  identi-
         fied by a unique event flag.  When the timer expires, MBLAST
         is entered, and retrieves the EFN  number  form  the  stack.
         The  EFN  is  located in tt-table, which gives access to the
         foo-count.  If the foo-count is zero, MBLAST resets the mum-
         ble  bit  for  that tt, and exits.  This clears mumble mode,
         allowing the next valid password to be accepted.  

              On the other hand, if the foo-count is non-zero, MBLAST
         adds the count to the total-foo (for logging purposes), cle-
         ars the foo-count, and re-issues  the  mark-time  directive.
         This perpetuates mumble mode for another interval.  



         2.1.3  Message Processing

              Messages are key to SCLI - as they inform  the  CLI  of
         system   actions   which  might  affect  terminal  security.
         Several operator-initiated messgaes are also accepted, which
         control SCLI functions.  

              SCLI makes great attempts to maintain it's control over
         protcted terminals.  Basic protection is provided by the op-
         erating system.  All input to a terminal goes to that termi-
         nal's   CLI,   without   exception   (the  standard  control
         characters like CTRL-U, -S, etc.  continue to  be  processed
         by  the  tt driver).  Also, a CLI is non-abortable - it must
         be  first  eliminated  before  the  task  can  be   aborted.
         Finally,  if  the  CLI  task  exits for some reason (such as
         fatal error), the executive will re-activate it when a  mes-
         sage or command is received for that CLI.  This more or less
         makes SCLI a crash-proof program.  SCLI is allowed to die on
         rare errors, such as low-pool conditions, without compromiz-
         ing security.  

              A cli may only be eliminated if no terminals are linked
         to  it.  SCLI goes beyond this protection by reacting to the
         'you have been eliminated' message with a RPOI of MCR to re-
         establish  the  cli.   This  occurrs very rapidly, providing
         good security (not perfect) against a fast typist's  'elimi-
         nate, abort' sequence.  

              The MCR SET command may be  used  (from  a  priveleged,
         logged-on terminal), to alter the CLI associated with a ter-
         minal.  SCLI reacts to this as well.  If a protected  termi-

         SCLI Narrative                                      Page 2-5
         



         nal  which  is not known by SCLI to be 'logged on', is reset
         to a different CLI, SCLI simply sets the  terminal  back  to
         SCLI with the SCLI$ directive.  

              .hl 2 User Messages

              There are currently three messages known to SCLI,  bey-
         ond the system-initiated ones.  THese are all issued via the
         MCR CLI /MESSAGE directive.   Two  messages  set  and  reset
         'verbose' logging.  Verbose logging is normally OFF (reset).
         When set, all invalid input to scli is passed on  in  a  log
         entry.  When reset, only the invalid command causing mumble-
         mode to be initiated is so logged.  

              The third user message provides the only known means to
         effect the orderly shutdown of SCLI.  When issued, this mes-
         sage sets a flag, telling SCLI to accept normally unfriendly
         behavior such as terminal CLI reassignment, and CLI elimina-
         tion.  Note that, even though  this  'maintenance  shutdown'
         mode  is  set by the message, security protection remains in
         effect until the user disconnects SCLI  from  the  protected
         terminals, and elimintates SCLI.  



         2.1.4  Logging

              Module LOG handles all logging functions.  A macro, de-
         fined  in SCLIDAT.MAC, eases the setup and call of LOG.  All
         logging is via pre-defined messages, with  variable  parame-
         ters.   The  DOLOG  macro  accepts  the message number and a
         message-specific parameter list.  

              Messages may be routed to either  the  console  (device
         CO:),  or  to  the  system error log file, or both.  Message
         routing is controlled by flag bits in the message definition
         (module  LOGMSG.MAC).   The  RSX $EDMSG routines are used to
         format the messages, handling all conversion  and  parameter
         substitution.  

              Since messages are routed through CO:, logging  is  de-
         pendent  upon the settings of the console output task (COT).
         Using the MCR SET /COLOG commands, it is possible  to  route
         console  messages to a terminal, a file, or both.  If COT is
         turned off entirely, messages will appear on the system con-
         sole device.  

              A later chapter covers the format and  content  of  all
         log messages in full detail.  

         
         





                                  CHAPTER 3

                                  Standards



         3.1  Coding standards

              This section presents coding and design standards to be
         followed for this project.



         3.1.1  Modularity

              This is a fully modular program.  Each source file must
         contain code for a single function.  This may include sever-
         al related subroutines, or a single routine.  An example  of
         the former might be the MUMBLE.MAC module, containing MBLON,
         MBLOFF, and MBLAST -- all routines  relating  to  initiating
         and  terminating  mumble  mode.  It would also be acceptable
         for these three routines to exist in separate source files. 



         3.1.2  Source Format

              Each source module will be maintained in a  SourceTools
         archive  (xxx.SCN  file).  File TEMPLATE.MAC will be used as
         the basis for all source files.  The  fields  surrounded  by
         tilde  characters (~) are supplied by GETSRC, and should not
         be altered.  

              There will be a module header for  each  routine.   The
         skeleton  header is provided by the CTRL-P command, assuming
         the system edt include file "MACRO"  is  used.   The  header
         shall  contain  the module title, a description of its func-
         tion, call site, input and output parameters,  and  register
         usage.   A  list  of  routines called will be included.  The
         description will include the module's  function,  error  re-
         turns, and algorithm if not self-evident.  



         3.1.3  Source Control

              This project is being implemented under the SourceTools
         system.   Every  source file will be under "SrcCon" control.
         New modules are to be entered into the system following ini-

         Standards                                           Page 3-2
         



         tial  test.  Subsequent modifications are to be under source
         control.  Test programs will also be  subject  to  the  same
         controls.



         3.1.4  Test Programs

              Most modules will  have  an  associated  test  program,
         which demonstrates the module functions.  Test programs need
         not exhaustively test the module, and should be as simple as
         is reasonable.  Extensive testing will be done during integ-
         ration.  

              Individual test programs may exercise multiple modules,
         so  long  as  it  remains  easy  to  determine the source of
         faults.  Test programs which evolve to test several  related
         modules are ideal.  



         3.1.5  PSECT Usage

              This section defines the PSECT (program section)  usage
         for the project.  

              1.  BLANK - all program code will reside in  the  blank
                  (default) psect.

              2.  GDATA - global common data (rw,  gbl,  ovr).   This
                  psect  defined by module SCLIDAT, which must be in-
                  cluded in the assembly of using modules.

              3.  DATA - global private data (rw, gbl).

              4.  LDAT - local data.  This psect shall be used by mo-
                  dules  for scratch storage - assume that it will be
                  destroyed across module invokations.  

              5.  DPBS - static directive DPBs - (rw, lcl)

              Except for GDATA, each module may contribute  to  these
         psects.   Data which is shared among modules must be defined
         in SCLIDAT.MAC.

              Psect DATA is global, concatenated, and may be used  by
         any  module  which  needs data to remain across calls to the
         module.  Psect LDAT is  overlaid  and  is  to  be  used  for
         scratch  storage.   The  contents of LDAT are undefined upon
         entry to a module.  


         Standards                                           Page 3-3
         



                                     NOTE

              Any program contributing to one of the data psects
              must  include an .EVEN directive following defini-
              tions for the psect.  This  forces  each  module's
              contribution  to be of even size, and prevents er-
              rors due to TKB's byte alignment of data psects.  



         3.1.6  Exceptions

              The only exceptions to the above standards are the mod-
         ifications  to DEC system software.  These modifications, to
         module TTMOD.MAC of the RSX terminal driver, and to BYE.MAC,
         shall  adhere to the format and standards employed by DEC in
         constructing and maintaining RSX system software.  Note that
         these  modules  stand alone from SCLI, even though the modi-
         fied programs are required for proper function of the  secu-
         rity  system.   Modificatons to TTDRV and BYE are documented
         in later chapters.  The related  files  (including  separate
         runoff  source files for each modification) are found in uic
         [1,101] (11MPLUS and common) and [1,102] (11M  specific)  on
         the SCLI sources disk.  

         
         





                                  CHAPTER 4

                                   Database



              This chapter describes the database used by SCLI.   The
         database  consists of global data defined in module SCLIDAT,
         internal error messages defined in ERNUM.TXT (these are  im-
         plicit  in  the  SCLI  code),  logging  messages  defined in
         LOGMSG.DAT, and the command table, defined in KEYTAB.  These
         are all internal databases - SCLI does no file operations of
         it's own.  



         4.1  Global Data

              Module SCLIDAT defines the global data for SCLI.   This
         module  must be included ( .include directive) in all source
         modules which must access the global database.  



         4.1.1  Constants

              A number of constants are defined.  Most of  these  de-
         fine  the  offsets and flag bit values for the tt-table, and
         the command table.   Three  additional  constants  tune  the
         mumble-mode functions.

              *  MAXFOO sets the trigger point for mumble mode.  When
                 more than maxfoo invalid commands are received, mum-
                 ble mode is entered.  This should  remain  a  fairly
                 small number (3-5).  
              *  MBLUNI defines the time units for the mumble  inter-
                 val timer.  This must have a value of 2 (seconds) or
                 3 (minutes).  
              *  MBLTIM defines the count  for  the  mumble  interval
                 timer.  A time interval of 2-5 minutes is suggested.



         4.1.2  TT-TABLE

              This table contains one entry per  protected  terminal.
         It  must  be terminated with a zero word.  Macro DEFTT, also
         defined in SCLIDAT, is used to construct the table.  A table
         entry contains the following fields:

         Database                                            Page 4-2
         



              *  tt.num - integer number of the terminal
              *  tt.foo - integer count of invalid commands

                      This value is incremented for each invalid com-
                 mand received from the terminal.  It is reset by the
                 mumble  timer  completion  routine  (MBLAST).   This
                 value must remain zero for an entire mumble interval
                 before MBLAST will reset mumble mode.  
              *  tt.efn - event flag used  in  mumble-mode  for  this
                 terminal
              *  tt.flg - flags word

                      tt.flg bits are:
                 *  fl.mbl - 1-> terminal is in mumble mode
                 *  fl.pro - 1-> this  terminal's  cli  is  currently
                    SCLI
              *  tt.uid - pointer to user-id string, or nil

                      This pointer is initialized when a user is  ad-
                 mitted  to the system.  It is then used when the use
                 loggs out (SCLI resumes control over the  terminal),
                 to write a log entry.  
              *  tt.tot - integer total foo count since last login

                      This value is maintained entirely  for  logging
                 purposes.   Since tt.foo is reset at the end of each
                 mumble interval, tt.tot is used  to  accumulate  the
                 total  number of invalid login attempts.  This value
                 is cleared when a user is admitted to the system.  



         4.1.3  Command Table

              There  are  two  command  tables  in  SCLI.   The  pre-
         encrypted  command strings are in a table defined locally to
         the LOOKUP subroutine.  Lookup returns an  index  into  this
         table, or zero if no entry is found.  

              The command table defined in SCLIDAT  contains  corres-
         ponding  entries.   The  index returned by LOOKUP is used to
         access CMDTBL.  Cmdtbl is also zero terminated, and constant
         MAXCMD   also  gives  the  address  of  the  end  of  table.
         Currently, only MAXCMD is used.  The fields of cmdtbl are as
         follows:

              *  cm.rpl - pointer to reply string

                      The reply string is issued to the user's termi-
                 nal  when this command is input, and the terminal is
                 NOT in mumble mode.  

         Database                                            Page 4-3
         



              *  cm.id - pointer to the plain-text  user  id  string.
                 This  string  is only defined for commands which are
                 valid passwords.  When the user is  logged  on,  the
                 user-id string is used to greet the user, and is en-
                 tered in a log entry.  The user-id is also saved  in
                 the  tt-table,  and appears in a logout message when
                 SCLI resumes control of the terminal.  
              *  cm.act  -  the  action  to  be   taken   when   this
                 command/message  is received.  There are two actions
                 only for command input:  ac.fai  and  ac.pas.   They
                 are  fail/pass respectively.  The presence of a fail
                 action allows dummy table entries.  Most often these
                 are  used  for  common  login sequences such as HEL,
                 LOGIN, etc.  This allows non-standard replys  to  be
                 issued for these commands.  

                      AC.MES  defines  the   first   message   entry.
                 Actions  greater  than or equal to ac.mes are by de-
                 finition messages received via the CLI /MESSAGE  fa-
                 cility.    The  first  such  message  has  the  same
                 commmand number as ac.mes.  Three messages  are  de-
                 fined  at  this  time:   ac.mai  enables maintenance
                 shutdown mode; ac.vrb enables verbose logging of in-
                 valid input; ac.qui disables verbose logging.  

              The first  entry  in  cmdtbl  is  required  to  be  the
         unknown-command  action.   Unknown  commands,  commands from
         non-protected terminals, and mumble-mode all use  the  reply
         string from this entry.  

              Other entries in the table may be  in  any  order,  al-
         though  by convention the message entries are grouped at the
         end of the table.  



         4.1.4  Reply Strings

              These are simply ASCIZ strings which are pointed to  by
         the command table entries.  There need not be a one-one cor-
         respondence between the  number  of  such  strings  and  the
         number  of  command  table  entries.  The reply string for a
         valid login command should be some sort of greeting  to  the
         user.  Other reply strings are up to the programmer.  




         Database                                            Page 4-4
         



         4.1.5  User-id Strings

              These are plain-text identifiers for each valid user of
         the system.  They are placed in log entries at login and lo-
         gout (to and from SCLI) time.  



         4.1.6  Global Variables

              Several variables are defined  in  SCLIDAT,  which  are
         used  globally.   Their  use  is fairly obvious.  One is the
         Flags word, consisting of  two  flag  bits  which  configure
         SCLI.   GF.KIL  is  the maintenance shutdown bit.  It is set
         when the ac.mai message is received by  SCLI,  and  disables
         several  protection  features.  When set, it it possible for
         the knowlegable user to shut down SCLI in an orderly manner.
         When  clear,  it is essentially impossible to shut SCLI down
         other than by pathological means.  

              The other flag bit is GF.VRB, which controls  the  ver-
         bose logging of invalid input commands.  



         4.2  Internal Errors

              Internal errors are logged through the same logging me-
         chanism (DOLOG) used for other activity.  Log message number
         9.  signifies an internal error log entry.  Because  parame-
         ters  must  be passed by reference, some care is required in
         setting up an internal error log entry.  A typical  internal
         error call is as follows:

                 mov     $dsw, p1
                 mov      1, nparm
                 mov      5, err
                 DOLOG   9.,<err,nparm,p1>

         where p1, nparm, and err are all variable labels.  Note that
         the  number  of  parameters beyond nparm is variable.  Nparm
         tells the log routine how many parameters to include in  the
         log  entry,  and how many to pull off the R5 stack.  Err and
         nparm themselves are always required, and are NOT counted in
         the value of nparm.  

              Due to limitations on log entry size,  only  the  error
         number and parameter values are logged.  File ERNUM.TXT, re-
         produced in an appendix, gives the error numbers, initiating
         routine, number of parameters, and their meaning.  Using the
         above example, error 5 is issued by SCLI upon failure to in-

         Database                                            Page 4-5
         



         itialize  (ALUN$)  the  console  LUN.   P1  is the directive
         status word.  



         4.3  Log Messages

              Log messages are defined  in  module  LOGMSG.MAC.   For
         each  message,  an ASCIZ string is defined, which is used as
         the 'control string' in an EDMSG call.  See the  RSX  System
         Library Reference Manual for the format and functions of the
         EDMSG routines.  

              Two other structures are associated with the  log  mes-
         sages.   Table msgtbl contains the pointer to the ASCIZ con-
         trol string for each message.  The strings are  accessed  by
         using the message number as an index into msgtbl, from which
         the string address is retrieved.  

              The other table, MSGFLG, is  a  byte  table  containing
         control  bits  for  each message.  It is also indexed by the
         message number.  The control bits specify  the  desitination
         of the message - the console, error logger, or both.  

              A  prefix  (PREMSG)  is  added  to  each   log   entry.
         Currently , the prefix consists of the word "SECURE:" only. 



         4.4  Key Table

              For security reasons, the text of commands and messages
         is  stored  internally  in encrypted form.  Input to SCLI is
         then encrypted using the same algorithm, and  the  scrambled
         text compared against the internal tables.  

              Module LOOKUP performs the encryption and table  lookup
         functions.   It  'includes' module KEYTAB.MAC, which defines
         the table.  KEYTAB.MAC is in turn produced by  program  KEY-
         GEN,  which takes input file KEYTAB.TXT (the plain text mes-
         sages), encrypts the text, and  writes  KEYTAB.MAC  as  it's
         output.  

              KEYTAB.MAC  defines  a  table  of  pointers  to   ASCII
         strings.   The  table entries must correspond to the entries
         in CMDTBL (defined in SCLIDAT).  It is critical  that  their
         be a one-one correspondence between KEYTAB and CMDTBL.  That
         is, each entry in CMDTBL must have a corresponding entry  in
         KEYTAB, and vice versa.  If these two tables are not confor-
         mant, SCLI will fail in various and often obscure ways.  

         
         





                                  CHAPTER 5

                           Maintenance Instructions



              This chapter contains sections  devoted  to  rebuilding
         and  modifying  SCLI.   It  will make reference to the USRSB
         routine and the modified BYE program, both of which are more
         fully  described  in a later chapter.  Also found in a later
         chapter are details of required  modifications  to  the  RSX
         terminal driver.  

              Maintenance functions for SCLI primarily  resolve  into
         three  areas:   protected  terminals,  passwords, and users.
         These areas can be expected to change for each installation.



         5.1  Protected Terminals

              The number and identity of terminals protected by  SCLI
         is   coded   in   two  areas:   first  in  the  tt-table  in
         SCLIDAT.MAC; second, in the USRSB  module  included  in  the
         modified  BYE  program.  It is necessary that both these mo-
         dules define the same terminals.



         5.1.1  USRSB

              USRSB contains a table (JMBTBL) with an entry for  each
         protected  terminal.   The  entry  consists  of the terminal
         number (an integer), and the default CLI  name  (in  RAD50).
         Macro  ENT  defined  in  USRSB.MAC  will construct a correct
         table entry.  It is normal to leave several empty entries in
         the table.  Having empty entries allows the table to be mod-
         ified using ZAP, without having to rebuild the BYE  program.
         BYE ignores any null entries in the table.  

              While it is necessary that each terminal  protected  by
         SCLI have an entry in JMBTBL, it is possible to use the same
         mechanism to change the default CLI for  other  (non-secure)
         terminals.  Thus, JMBTBL may have additional entries, refer-
         encing CLIs other than SCLI.  Such entries will  not  effect
         security  operations.   Whenever  a terminal logs off (using
         the BYE program), BYE checks the table for a terminal number
         match.   If  a  match  is  found, BYE forces the CLI to that
         given in the table.  The effect is to have the CLI for  that

         Maintenance Instructions                            Page 5-2
         



         terminal  as  other than MCR whenever the terminal is logged
         off.  



         5.1.2  SCLIDAT

              As previously described, SCLIDAT defines  TTTBL,  which
         has  an  entry for each protected terminal.  It is necessary
         that any terminal with the default CLI of SCLI have an entry
         in  TTTBL.   If  a mismatch between TTTBL and JMBTBL occurs,
         either the CLI will not be re-established on logout, or SCLI
         will never allow access through the terminal.  In the latter
         case, SCLI will issue an error message "Message from unknown
         terminal".

              It is possible to alter TTTBL using ZAP, but the normal
         mode will be to rebuild SCLI after editing SCLIDAT.  



         5.2  Passwords

              Passwords are defined by KEYTAB.TXT.  These  are  ASCII
         strings,  up  to 72.  characters in length.  The key strings
         may contain any printable  character  (including  tab),  and
         some  control characters (those which are not intercepted by
         the terminal driver).  CASE IS SIGNIFICANT!  Unlike the  MCR
         interface, which automatically converts input to upper case,
         the SCLI interface accepts upper or lower case.   This  fact
         should be used in designing passwords.  

              Passwords should be phrases, and should be at least 10-
         12 characters in length.  

              To alter a password, edit KEYTAB.TXT to define the  ap-
         propriate  plain-text  string.   Recall  that the entries in
         KEYTAB correspond to the command table entries  in  SCLIDAT.
         Once KEYTAB.TXT is as desired, run program KEYGEN.  The nor-
         mal command to KEYGEN is:

         KGN>KEYTAB.MAC=KEYTAB.TXT

         KEYGEN will write the output file containing  the  encrypted
         text  strings.   For  further information on KEYGEN, see the
         source file KEYGEN.MAC.  

              Once KEYGEN.MAC has  been  created,  reassemble  module
         LOOKUP,  which  is the only module to include KEYTAB.  Then,
         rebuild SCLI.  


         Maintenance Instructions                            Page 5-3
         



                                     NOTE

              All  that  is  really  required  is  the  edit  of
              KEYTAB.TXT.  Then, use the MAKE program to rebuild
              SCLI.  MAKE will detect the new KEYTAB, run KEYGEN
              (rebuilding IT if necessary), and rebuild SCLI.  



         5.3  Command Table

              The command table in SCLIDAT  defines  the  known  com-
         mands,  and  the action to be taken.  Probably the most fre-
         quent alterations will be to the uiser-id strings.  

              Again, it is necessary  to  maintain  a  correspondence
         between the entries in CMDTBL and those in KEYTAB.  



         5.4  Summary

              This section summarizes the required  edits  to  effect
         various configuration changes to SCLI.  



         5.4.1  Change Terminals

              To alter the protected terminals, JMBTBL in  USRSB  and
         TTTBL in SCLIDAT must be modified.  Rebuild BYE and SCLI.



         5.4.2  Change Passwords

              To alter password text, for either  input  commands  or
         messages,  edit module KEYTAB.TXT.  Then, run KEYGEN to cre-
         ate KEYTAB.MAC.  Reassemble LOOKUP, then rebuild SCLI.



         5.4.3  Change Users

              To change a user's id string, edit the string in  SCLI-
         DAT,  and/or  the string pointer in CMDTBL, also in SCLIDAT.
         Rebuild SCLI.  

              To add or remove a user, edit CMDTBL in SCLIDAT, possi-
         bly  adding  a  user-id string.  Edit KEYTAB.TXT to maintain
         correspondence between password strings  and  command  table

         Maintenance Instructions                            Page 5-4
         



         entries.  To rebuild, follow instructions above for changing
         passwords.  



         5.4.4  Change Messages

              The procedure for adding or modifying messages  is  es-
         sentially the same as that for user-ids, as described above.
         The message text is in KEYTAB, while the corresponding  com-
         mand table entry is in SCLIDAT.  



         5.5  Build Instructions

              SCLI is composed of three components:   the  SCLI  task
         itself,  the  modified  BYE  task,  and  the  modified TTDRV
         driver.  Each is built in a separate  operation.   For  most
         maintenance  operatons,  it will not be necessary to rebuild
         all three components.  

              SCLI will normally be installed by copying  the  source
         kit  to  the SYSGEN work disk for the target system.  If ne-
         cessary, copy all files in uic [1,100], [1,101], and [1,102]
         from the SCLI kit to the target disk.  The following discus-
         sion assumes that these accounts do in fact exist on a  sys-
         gen  work  disk.   The  process  is similar for other source
         locations.  

              It is also assumed that required modifications  to  the
         sources  have been made, and the archive (.scn) files updat-
         ed.  



         5.5.1  SCLI

              SCLI rebuild is controlled by the sourcetools MAKE pro-
         gram.   Use  of MAKE greatly simplifies the rebuild process.
         To rebuild SCLI, enter the following MCR commands:

              1.  SET /UIC=[1,100]

              2.  @MAKE SCLI

              When the command file completes, copy SCLI.TSK  to  the
         library account on the target system disk.  




         Maintenance Instructions                            Page 5-5
         



         5.5.2  Documentation

              SCLI documentation can be rebuild manually from the ar-
         chive  files.  Simply GET the required modules and pass them
         through RNO.  A full documentation set may be built with the
         following MCR commands:

              1.  SET /UIC=[1,100]

              2.  MAK SCLIDOC.CMD=SCLI/target:"Dockit"

              3.  @SCLIDOC.CMD

              Be warned that some of the runoff source files  include
         (.require) additional runoff sources.  Users unfamiliar with
         the sources should either rebuild the entire  kit,  as  des-
         cribed above, or examine the source files to ensure that the
         required include files are present.  

              Individual documents may  be  rebuilt  by  substituting
         their   name   for   the   'target'   above.    For  example
         /target:"Scliman.doc" would produce this manual.  



         5.5.3  BYE

              BYE is built in [1,101] (M+) or [1,102] (M), and copied
         to  the library account of the target disk.  BYEASM.CMD will
         assemble BYE.  

              USRSB is reassembled as follows:

         GET USRSB
         MAC USRSB,USRSB=USRSB


              TKB @BYE2BLD will rebuild  BYE2.TSK.   BYE2BLD  assumes
         that  device  TK:  points to the sysgen work disk (to obtain
         RSX11M.STB, MCR.OLB, etc), and that  BYE.OBJ  and  USRSB.OBJ
         are in the current account.  It leaves BYE2.TSK and BYE2.MAP
         in the current account.  



         5.5.4  TTDRV

              The terminal  driver  modification  is  not  automated.
         Normally,  the  modified  source  file  will  be copied from
         [1,101] (or [1,102]) into [11,10] of the sysgen  disk  prior
         to  SYSGEN.   SYSGEN  then builds the modified driver by de-

         Maintenance Instructions                            Page 5-6
         



         fault.  If the modification must be done after  SYSGEN,  the
         following  instructions  should  be followed for MPLUS.  The
         procedure for M is similar.  

              1.  Copy TTMOD.MAC and  TTMODASM.CMD  from  [1,101]  to
                  [11,10].  

              2.  Execute MAC @TTMODASM, from [11,10].

              3.  From [1,24]:  LBR TTDRV/RP=[11,24]TTMOD.

              4.  From [1,24]:  TKB @[200,200]TTDRVBLD

              5.  Use VMR to UNLoad the old driver and LOAd the modi-
                  fied one.  



         5.6  Initialization

              SCLI should be installed with the CLI=YES option either
         in  VMR  or  STARTUP.CMD.   Very  early in STARTUP.CMD, file
         STARTSCLI.CMD should be executed.  Logons should be disabled
         until after STARTSCLI is executed.  Alternately, SCLI may be
         initialized directly from STARTUP.CMD, using STARTSCLI as an
         example of the commands.  

              It is important that the proper switches be included in
         the  CLI  command  initializing SCLI.  If "/QUI/MES/LGO" are
         not present, the security system will not function properly.
         In  most cases, the protected terminals will become unusable
         (usually slaved).  The prompts may be changed as desired.  

         
         





                                  CHAPTER 6

                             Module Descriptions



              This chapter contains a section for each module in  the
         system,  excepting  test programs.  The information in these
         sections is essentially a duplicate of the  header  informa-
         tion in the source module.  



         6.1  Global Data

              Module SCLIDAT defines the global database for the SCLI
         program.   This  file is "included" (.INCLUDE or in assembly
         command line) in any source program which requires access to
         the  global data.  Note that many modules do not require ac-
         cess to the global data.



         6.2  CRYPT	

         Crypt performs a simple, in-place encryption  of  the  input
         string.   The algorithm is the familiar and relatively inse-
         cure XOR of data bytes with a  key  text.   This  works  for
         crypt  because  the  key is guaranteed to be longer than the
         input text, and the messages  are  relatively  short.   Both
         combine  to  frustrate normal breaking techniques.  If r0 is
         odd, the first character of the key is skipped, resulting in
         word alignment for most of the routine.  
          
         	CALL
         		jsr pc,CRYPT
         	INPUT
         		r0 -> input string
         		r1 =  length of input string
          
         	OUTPUT
         		input string encrypted in place
          
         	REGS
         		all preserved

              Program TSCRYPT exercises this routine.  

         Module Descriptions                                 Page 6-2
         



         6.3  DOMSG

         DOMSG processes all messages (as opposed  to  commands)  re-
         ceived by SCLI.  Messages come in two forms:  those produced
         automatically by RSX, and those initiated by  someone  using
         the MCR "CLI /MESSAGE" command.  Both types are important to
         SCLI.  

                 CALL
                         jsr pc, domsg
                 INPUT
                         r0 -> GCCI command buffer
                 OUTPUT
                         various (including immediate exit)
                         depending upon message received.
                 REGS
                         preserved

         Module Descriptions                                 Page 6-3
         



         6.4  LOG

         LOG logs messages to the  error  logging  file  (via  SMSG$)
         and/or  to  the console (CO).  For testing, if logtt3 is de-
         fined (just before entry point), logs all  messages  in  raw
         form  to  LUN   3,  which is hardcoded to TT3.  Messages are
         identified by number.  A variable number of  parameters  are
         required  depending  upon the message.  For message numbers,
         required parameters, see module LOGMSG.MAC.  Message  number
         is  a pass-by-value.  All of the variable params are pass by
         reference.  
          
                 CALL
                         call r5,log,<msg,params>
                         msg = message number (messages defined
          above)
                         params = parameters dependant upon message
          number
                                  see individual message definition
          above
          
                 INPUT
                         params on r5 stack
          
                 OUTPUT
                         message formatted and logged as indicated by
          flags word
                         in message database (defined above)
          
                 REGS
                         preserved
          
                 CALLS
                         uses $EDMSG from SYSLIB to format messages
                         includes LOGMSG.MAC to define messages



         6.4.1  Notes

              LOG does a QIO no-wait to CO:, followed by a mark-time.
         Both  specify  AST  routines.  Whichever one completes first
         cancells the other.  This provides output timeout  services,
         since a hung QIOW to CO:  would hand the entire SCLI system.

              LOG also contains code to fake out a call to itself  in
         the  event  of an internal error.  This code is a bit wierd,
         in that it must protect against infinite looping on multiple
         errors.  However, it is known to work.  

         Module Descriptions                                 Page 6-4
         



         6.5  LOOKUP

              LOOKUP is called with a    plain-text command line.  It
         first  encrypts the command line, then searches the password
         table for a match.  LOOKUP returns the offset of the  match-
         ing  entry  in the command table, or 0 (zero) if no matching
         entry exists.  Also, a no-match condition returns carry set.


                                     NOTE

              The returned index is the  byte  offset  into  the
              command table (NOT the password table).  The pass-
              word table contains one less entry (the entry with
              index=0) than the command table.  In simple terms,
              add the base of the command table to r2 on  return
              and look at the command.  


         	CALL
         		jsr pc, lookup
         	INPUT
         		r0 -> command line
         		r1 = length of command line
         	OUTPUT
         		r0 -> same command line, but encrypted now
         		r2 = command index (0 -> no match)
         		carry set -> no match
         		carry clear -> match found
         	REGS
         		r2 modified, string referenced by r0 modified
         		others preserved
          
         	CALLS
         		CRYPT
          

              NOTES:

              1.  In order to work properly, trailing whitespace (tab
                  or  space)  should  be  stripped from command line.
                  Leading whitespace is ok, allowing tricky passwords
                  like <tab><tab>hi there!

              2.  Source module KEYTAB.MAC is .INCLUDED in  this  mo-
                  dule.  It is generated by KEYGEN.  

              Program TSTLOOKUP exercises this module.  

         Module Descriptions                                 Page 6-5
         



         6.6  MUMBLE

              Module MUMBLE.MAC contains  two  routines:   MBLON  and
         MBLAST.   Together these routines implement mumble mode ser-
         vices.  

              MBLON initiates mumble mode for the  current  tt.   The
         current tt is pointed to by ttptr (defined by sclidat).  
                 CALL
                         jsr,pc mblon
          
                 INPUT
                         ttptr -> tt record to be put in mumble mode
          
                 OUTPUT
                         tt placed in mumble mode,
                         foo-count added to total for tt
                         foo-count for tt cleared
                         mumble-timer started for tt's efn
                 REGS
                         preserved

              MBLAST is entered upon expiration of  the  mumble-timer
         for  a  given tt.  The associated tt is determined, and it's
         foo-count examined.  Either the mumble-timer is perpetuated,
         or the tt is kicked out of mumble-mode.
          
                 CALL
                         AST service routine
          
                 INPUT
                         on stack: efn (remove before exit)
          
                 OUTPUT
                 
                         if tt.foo > 0 
                                 mumble-timer restarted
                         if tt.foo = 0 
                                 mumble-mode cleared
          
                         in either case
                                 tt.foo added to tt.tot, then cleared
          
                 REGS
                         preserved

         Module Descriptions                                 Page 6-6
         



         6.7  SLEN

              SLEN determines the length of an asciz  string.   ASCIZ
         strings  are  terminated  by a null (zero) byte.  Length re-
         turned does not include the null byte.  
          
         	CALL
         		jsr pc, SLEN
         	INPUT
         		r0 -> input string
          
         	OUTPUT
         		r0 -> input string
         		length on stack
          
         	REGS
         		all preserved
          
         	NOTE: 	1. Caller must pop length off of stack on return
         		2. Input string had better have a null terminator!
          

              Program TSTSLEN exercises this routine.  

         Module Descriptions                                 Page 6-7
         



         6.8  TYPE

              TYPE outputs a message to one of  two  terminals:   the
         CLI  command input terminal, or the task ti:.  The latter is
         assumed pointed to by LUN 5.  For the former,  the  terminal
         is  in  the  GCCI  buffer pointed to by r0, and LUN 1 is as-
         signed to that terminal.

              TYPE uses QIO (no-wait), with MRKT, in order to provide
         positive  timeout  action.   In  the event the qio times-out
         (user hit no-scroll for example, or hung  up),  the  QIO  is
         killed.  No other error reporting is done, to prevent an in-
         finite error loop!
          
         	CALL
         		CALL TYPE,r5,buf,flag
          
         	INPUT
         		r0 -> GCCI return buffer 
         		      (reqd if cli command term is output)
         	on r5 parameter list -
         		buf -> ASCIZ buffer to output
         		flag = 0 --> use cli command term
         		     = 1 --> output to TI:
          
         	OUTPUT
         		message sent, errors ignored (!)
         		if flag = 0, LUN 1 set to comand input terminal
          
         	REGS
         		preserved

              Program TSTTYPE exercises this module.  

         
         





                                  CHAPTER 7

                                Test Programs



         This chapter contains brief descriptions of  the  test  pro-
         grams used to validate the various modules.  



         7.1  TSTCRYPT

              This program validates the CRYPT module.  It accepts  a
         line  of input from the terminal, encrypts it, then decrypts
         it.  The input and decrypted text are printed on the  termi-
         nal,  along  with  the  result of a check that the encrypted
         text does NOT match the input.  Note that TSTCRYPT does  not
         validate  the  encryption algorithm for security - only that
         it will decrypt a duplicate of the original plain text.  



         7.2  TSTLOG

              TSTLOG exercises the logging  facility.   It  basically
         calls  LOG  once per message type.  Several 'internal error'
         messages are logged, in order to exercise the variable  par-
         ameter  features.  Output from tstlog will be on the console
         log and error log.  This is a useful program  for  producing
         sample log reports as well.  



         7.3  TSTLOOKUP

              This program validates LOOKUP, and indirectly CRYPT and
         KEYGEN.  It accepts a string from the operator, passes it to
         lookup, and prints the returned index value.  CTRL-Z  termi-
         nates.   The  returned  value is zero if no record found, or
         the byte offset into a table of responses.  It is just  pos-
         sible, especially if the STARTUP.CMD file is faulty, or fol-
         lowing maintenance shutdowns, that a user may be  logged  on
         to the terminal at the time SCLI takes control.  This is the
         only time that this situation can arrise.  In the event this
         happens,  the  user must satisfy SCLI, in order to return to
         MCR.  



         Test Programs                                       Page 7-2
         



         7.4  TSTTYPE

              This program validates TYPE.   It  dummies  up  a  GCCI
         buffer  with  device  info (HARDWIRED to tt23:!), then calls
         TYPE twice.  First, a message to the 'command  tt'  (tt23:),
         next a call to the 'task ti:'.  We don't try to exhaustively
         exercise the various error conditions, since most are  fatal
         anyway.   You  can  check  the timeout by hitting S on tt23:
         before running the program.



         7.5  TSTSLEN

              This program validates SLEN.   It  accepts  a  line  of
         input from TI:, and prints its length as returned by SLEN.  

         
         





                                  CHAPTER 8

                        Terminal Driver Modifications



              This chapter discusses the  modifications  to  the  RSX
         terminal  driver  required  to  support  the security system
         (SCLI) for remote dial-up lines.  



         8.1  Overview

              The RSX-11 (M and M+) terminal  driver  unconditionally
         forces  MCR  to  a terminal being answered on a remote line.
         While intended to provide a consistent interface  to  remote
         terminals,  this  functionality  breaks the security system,
         which depends upon  SCLI  owning  any  protected  terminals.
         Equally  unfortunate is the fact that TTDRV does not use the
         normal SCLI$ mechanism to establish MCR, but instead  simply
         hammers the executive data structures directly.  The exec is
         thus unaware that a port's CLI has changed, and does not in-
         form  SCLI of the action.  This prevents SCLI from re-taking
         the port.  

              Fortunately, a very simple patch to the terminal driver
         will  'correct'  this  situation.   The  remainder  of  this
         chapter describes the modification,  and  includes  instruc-
         tions  for making the patch either in the sources or via ZAP
         to an existing system.  



         8.2  Modification Details

              The relevant code is in subroutine MANS (modem answer),
         in  module TTMOD.MAC.  This file can be found on the distri-
         bution kits in [11,10].  MANS is called when a  remote  line
         is  answered  (e.g.,  carrier  detected).  Its purpose is to
         place the terminal in a known (and benign) state.  MANS mod-
         ifies the terminal characteristics words, sets the buffer to
         72., and forces the CLI to MCR.  It then initiates  autobaud
         (if the terminal is set ABAUD), and returns.  

              The switch to MCR is accomplished by  one  of  two  in-
         structions, depending upon certain SYSGEN conditionals.  For
         MPLUS, this is a BIC instruction, while for M it  is  a  MOV
         instruction.   Both  are  commented  as  "SET  MCR  AS CLI".

         Terminal Driver Modifications                       Page 8-2
         



         Comment out these instructions.

              The driver also resets  the  lower-case  bit,  enabling
         lower-to-upper   case   conversion.   Since  SCLI  is  case-
         sensitive, we wish the terminal  to  be  left  in  lowercase
         mode.   This is accomplished by locating the BIC instruction
         containing "U2.LWC" in the first operand.  Remove the refer-
         ence to "U2.LWC", leaving the other bits intact.  


                                     NOTE

              Several other characteristics are set in this code
              section.   Most  may  be  eliminated, if it is de-
              sired.   Examples  include  U2.CRT,  U2.ESC,   and
              S3.8BC.   It is also possible to alter the default
              buffer size.  The buffer size must be at least 72.
              for SCLI to operate properly.



         8.3  Source Modification

              The desired method of modifying the driver  is  at  the
         source level.  UIC [1,101] contains the MPLUS files; [1,102]
         those for M.  These uics contains the modified TTMOD.MAC, an
         unmodified TTMOD.VGN, and TTMOD.COR.  

              Although M and M+ share the same source module, the up-
         date  versions  are  different, requiring patch sets in both
         [1,101] and [1,102].  The patches may have  to  be  manually
         applied,  and  new correction files built, for later updates
         or releases.   Both  patch  sets  contain  the  audit  trail
         "JMB227".

              The simplest way to apply these patches is to copy  the
         modified  TTMOD  to [11,10] of the sysgen work disk prior to
         SYSGEN.  Since TTDRV is always  re-assembled  and  built  by
         SYSGEN,  this will incorporate the patches.  It is also pos-
         sible to manually assemble TTMOD, and  rebuild  TTDRV  post-
         SYSGEN.   Follow  the  instructions in the release notes for
         rebuilding a driver.  The database doesn't change, so it  is
         possible  to  use  VMR to UNLoad and LOAd the patched driver
         without creating a new system image.  

              The secure source accounts contain TTMODASM.CMD,  which
         will reassemble TTMOD.  This file assumes that TTMOD.MAC ex-
         ists in [11,10] on the sysgen work disk, which is  also  the
         current  SY:.  Replace module TTMOD in [1,24]TTDRV.OLB, then
         rebuild.  To rebuild TTDRV, use [200,200]TTDRVBLD.CMD.  


         Terminal Driver Modifications                       Page 8-3
         



         8.4  Patching TTDRV.TSK

              It is also possible to apply these patches to TTDRV.TSK
         using  ZAP,  or to a running system using OPEN.  In order to
         do this, TTDRV.MAP, plus an assembly listing  of  TTMOD  are
         required.   The  patches add no code, and are thus simple to
         make.  Simply comment out the  "SET  MCR"  instruction  (all
         three  words!),  and  alter the bitmask for the BIC instruc-
         tion.  

              The unmodified  bitmask  is  currently  3047,  and  the
         patched value 3046.  


         
         





                                   CONTENTS



         1.  Introduction . . . . . . . . . . . . . . . . . . . . 1-1

             1.1  Overview  . . . . . . . . . . . . . . . . . . . 1-1
         
         2.  SCLI Narrative . . . . . . . . . . . . . . . . . . . 2-1

             2.1  SCLI Walkthru . . . . . . . . . . . . . . . . . 2-2
                  2.1.1  Command Input  . . . . . . . . . . . . . 2-3
                  2.1.2  Mumble Processing  . . . . . . . . . . . 2-3
                  2.1.3  Message Processing . . . . . . . . . . . 2-4
                  2.1.4  Logging  . . . . . . . . . . . . . . . . 2-5
         
         3.  Standards  . . . . . . . . . . . . . . . . . . . . . 3-1

             3.1  Coding standards  . . . . . . . . . . . . . . . 3-1
                  3.1.1  Modularity . . . . . . . . . . . . . . . 3-1
                  3.1.2  Source Format  . . . . . . . . . . . . . 3-1
                  3.1.3  Source Control . . . . . . . . . . . . . 3-1
                  3.1.4  Test Programs  . . . . . . . . . . . . . 3-2
                  3.1.5  PSECT Usage  . . . . . . . . . . . . . . 3-2
                  3.1.6  Exceptions . . . . . . . . . . . . . . . 3-3
         
         4.  Database . . . . . . . . . . . . . . . . . . . . . . 4-1

             4.1  Global Data . . . . . . . . . . . . . . . . . . 4-1
                  4.1.1  Constants  . . . . . . . . . . . . . . . 4-1
                  4.1.2  TT-TABLE . . . . . . . . . . . . . . . . 4-1
                  4.1.3  Command Table  . . . . . . . . . . . . . 4-2
                  4.1.4  Reply Strings  . . . . . . . . . . . . . 4-3
                  4.1.5  User-id Strings  . . . . . . . . . . . . 4-4
                  4.1.6  Global Variables . . . . . . . . . . . . 4-4
             4.2  Internal Errors . . . . . . . . . . . . . . . . 4-4
             4.3  Log Messages  . . . . . . . . . . . . . . . . . 4-5
             4.4  Key Table . . . . . . . . . . . . . . . . . . . 4-5
         
         5.  Maintenance Instructions . . . . . . . . . . . . . . 5-1

             5.1  Protected Terminals . . . . . . . . . . . . . . 5-1
                  5.1.1  USRSB  . . . . . . . . . . . . . . . . . 5-1
                  5.1.2  SCLIDAT  . . . . . . . . . . . . . . . . 5-2
             5.2  Passwords . . . . . . . . . . . . . . . . . . . 5-2
             5.3  Command Table . . . . . . . . . . . . . . . . . 5-3
             5.4  Summary . . . . . . . . . . . . . . . . . . . . 5-3
                  5.4.1  Change Terminals . . . . . . . . . . . . 5-3
                  5.4.2  Change Passwords . . . . . . . . . . . . 5-3

         
         



                  5.4.3  Change Users . . . . . . . . . . . . . . 5-3
                  5.4.4  Change Messages  . . . . . . . . . . . . 5-4
             5.5  Build Instructions  . . . . . . . . . . . . . . 5-4
                  5.5.1  SCLI . . . . . . . . . . . . . . . . . . 5-4
                  5.5.2  Documentation  . . . . . . . . . . . . . 5-5
                  5.5.3  BYE  . . . . . . . . . . . . . . . . . . 5-5
                  5.5.4  TTDRV  . . . . . . . . . . . . . . . . . 5-5
             5.6  Initialization  . . . . . . . . . . . . . . . . 5-6
         
         6.  Module Descriptions  . . . . . . . . . . . . . . . . 6-1

             6.1  Global Data . . . . . . . . . . . . . . . . . . 6-1
             6.2  CRYPT	  . . . . . . . . . . . . . . . . . . . . 6-1
             6.3  DOMSG . . . . . . . . . . . . . . . . . . . . . 6-2
             6.4  LOG . . . . . . . . . . . . . . . . . . . . . . 6-3
                  6.4.1  Notes  . . . . . . . . . . . . . . . . . 6-3
             6.5  LOOKUP  . . . . . . . . . . . . . . . . . . . . 6-4
             6.6  MUMBLE  . . . . . . . . . . . . . . . . . . . . 6-5
             6.7  SLEN  . . . . . . . . . . . . . . . . . . . . . 6-6
             6.8  TYPE  . . . . . . . . . . . . . . . . . . . . . 6-7
         
         7.  Test Programs  . . . . . . . . . . . . . . . . . . . 7-1

             7.1  TSTCRYPT  . . . . . . . . . . . . . . . . . . . 7-1
             7.2  TSTLOG  . . . . . . . . . . . . . . . . . . . . 7-1
             7.3  TSTLOOKUP . . . . . . . . . . . . . . . . . . . 7-1
             7.4  TSTTYPE . . . . . . . . . . . . . . . . . . . . 7-2
             7.5  TSTSLEN . . . . . . . . . . . . . . . . . . . . 7-2
         
         8.  Terminal Driver Modifications  . . . . . . . . . . . 8-1

             8.1  Overview  . . . . . . . . . . . . . . . . . . . 8-1
             8.2  Modification Details  . . . . . . . . . . . . . 8-1
             8.3  Source Modification . . . . . . . . . . . . . . 8-2
             8.4  Patching TTDRV.TSK  . . . . . . . . . . . . . . 8-3