PAL8XR      V02








     A PDP-8/INTERSIL 6100 cross-assembler implemented
             on a PDP-11 operating under RT-11










                    Author: B. R. Bergen
               (University of Massachusetts)
                 Revised by: R. D. Beattie
                        (C.S.I.R.O.)

               Revision date: 21st June 1978.





             CSIRO Division of Mineral Physics
                        P.O. Box 136
                         North Ryde
                    NSW, AUSTRALIA, 2113















     This program is a revision of PAL8,11 (DECUS program No. 11-201).
     Documentation prepared using RT-11 RUNOFF (DECUS 11-314).









  PAL8XR X-ASSEMBLER                                          Page   1



  1. INTRODUCTION

          PAL8XR V02 is an  assembler  for  a  PDP-8  minicomputer  or
     INTERSIL  6100  microprocessor,  that  will  execute  on a PDP-11
     operating under RT-11.  With the  exceptions  of  the  variations
     listed in this manual, it is compatible with the PAL III assembly
     language.  The assembler is a revision of PAL8,11 (DECUS 11-201),
     and   is   almost  identical  to  that  program  apart  from  the
     modification of the I/O routines to conform to  RT-11  practices.
     This  write-up  assumes  the  user  is  familiar with the PAL III
     assembler and the RT-11 operating system.


  2.  REQUIREMENTS

          Any valid RT-11 system; RT-11 V02C or  later.   The  program
     requires  4.5k  words  of  free memory, plus additional space for
     non-resident device handlers.

          The symbol table has space for 512.  symbols.  If the  table
     overflows  or if there is insufficient memory to run the program,
     the symbol table allocation can be changed by altering the  value
     of TOPROG on Page 1 of PAL8XR.MAC and re-assembling the file.


  3.  DOCUMENTATION

     The distribution medium contains the .MAC,.SAV,.LST,.RNO and .DOC
     files  for  the  program  PAL8XR.   The  .LST  file  is  a  cross
     referenced assembler listing of the program.  The .RNO  and  .DOC
     files   are   input   and   output  files  respectively  for  the
     documentation program PDP-11 RUNOFF (DECUS No.  11-314).






























  PAL8XR X-ASSEMBLER                                          Page   2



  4.  PAL8XR ASSEMBLY DIRECTIVES

     The following assembly directives are available in PAL8XR:

     DECIMA(L) - changes the assembly radix to decimal.

     OCTAL - changes the  assembly  radix  to  octal.   The  radix  is
             initially set to octal.

     FIELD x - used by the extended memory  loader.   Causes  a  field
             setting  'x'  to  be  output  on  the binary output.  The
             assembler origin is reset to 0200.  'x' must be between 0
             and 7 inclusive.

     PAUSE - indicates an end of file (EOF) condition.  The  assembler
             continues the assembly from the next open input file.

     Z x   - causes the assembler to  reserve  'x'  words  of  zeroes,
             starting  at  the  word indicated by the current location
             counter.  

     I     - sets the indirect bit (bit #3) in the assembled word

     PAGE  - terminates current memory page and advances the  assembly
             location counter to the next page in memory.

     FIXMRI x=y - defines 'x' as a memory reference instruction with a
             value   of  'y'.   Must  immediately  follow  an  EXPUNGE
             before any other symbols are defined.

     EXPUNG(E) - expunge  the  entire  symbol  table  apart  from  the
             pseudo-instructions.  

     FIXTAB -  fix  the  symbol  table.   Adds  the  preceding  symbol
             definitions  to  the  assembler's permanent symbol table.
             Symbols that have been fixed will not be printed  in  the
             symbol table listing at the end of PASS 3.  


     Single character operators:

            $ - end of pass (i.e. program)
            * - origin setting
            + - addition
            - - subtraction
            , - direct assignment
            . - current location counter
            / - enter comment field
            = - parameter assignment
            ; - treat as <EOL>












  PAL8XR X-ASSEMBLER                                          Page   3



  5.  COMPATIBILITY WITH PAL III

     The program  is  compatible  with  PAL  III  with  the  following
     exceptions:

  a) Multiple assignment statements may go beyond 2 levels.  e.g:

                    BOB=A=PDQ-LOOP=3776

     is a line and all symbols will receive the value 3776.

  b) The PAGE pseudo-op will advance the current location  counter  to
     the beginning of the next page in memory.  It may not be followed
     by an argument.

  c) The PAUSE pseudo-op causes the assembler to take input  from  the
     next open input file.

  d) A fatal  error  exit  will  occur  when  there  is  symbol  table
     overflow.  A message is printed as in PAL III.

  e) The FIELD pseudo-op will reset the location counter to 200.

  f) Input can be from any RT-11 supported mass-storage device.  There
     can  be  up to 5 input files, with the last file being terminated
     by a '$' and the preceding files  being  either  unterminated  or
     terminated  with  PAUSE  statements.   Output can be to any RT-11
     supported output device.  Input and  output  file  specifications
     are  input  via  the  RT-11 Command String Interpreter (CSI) (see
     Section 5).

  g) A symbol table listing can be obtained on PASS 3 by means of  the
     /S  CSI  switch.   (See Section 5).  In the symbol table listing,
     numbers  come  alphanumerically  before  letters.   Symbols   are
     printed four to a line instead of one to a line.

  h) Symbol capacity is 5 user defined symbols.

  i) The character set is the same with the following exceptions:

     TAB(11) is expanded to an 8 space tab stop on output.

     FORM-FEED (14) advances the PASS 3 output to the beginning of the
     next  page  and causes the page header to be printed.  <FF>'s are
     simulated by 4 <CR><LF>'s if the /F switch option is specified in
     the  CSI  command  string.   Pages are 66 lines long, including 2
     lines of page header and 4 lines of <FF> simulation















  PAL8XR X-ASSEMBLER                                          Page   4



  6.  OPERATING PROCEDURES

  a) Ensure that the cross assembler file PAL8XR.SAV  is  resident  in
     the system.

  b) Start the assembler by typing R PAL8XR if PAL8XR.SAV  is  on  the
     system  disk,  or  RUN DEV:PAL8XR if it is on a device other than
     the system disk.  The program will respond with an '*'.

  c) Enter the input and output  file  specifications  by  typing  the
     following command string:

            BINOUTSPEC,LISTOUTSPEC=INFLSPEC1,INFLSPEC2,..../S/F<CR>

     The default file extensions are :

            Binary output        .BI8
            Listing output       .LS8
            Input files          .PD8

     The file extensions must be included in  the  command  string  if
     they differ from these values.  There can be up to 5 input files.
     If either, or both of the output files are not  required,  simply
     omit  that  file specification from the command string.  e.g.  if
     you type:

               =INFLSPEC1,INFLSPEC2,.....<CR>

     the assembler will only execute PASS 1, which includes a  listing
     of  any  undefined  addresses,  illegal  instructions  etc.   The
     inclusion of the /S option  causes  the  assembler  to  output  a
     symbol table listing at the end of PASS 3 (if an assembly listing
     was also requested).  The /F option causes <FF>'s in the  listing
     file to be simulated by 4 <CR><LF>'s.

  d) The assembler will execute the desired passes, and on  completion
     will  respond  with  another  '*',  at which stage it is ready to
     accept another command string.

  e) It will be necessary to re-format the binary output file if it is
     to  be  used  for  PROM  programming.   Consult the relevant PROM
     Programmer manual to get the correct format.




















  PAL8XR X-ASSEMBLER                                          Page   5



  7.  ASSEMBLER OPERATION

          During PASS 1, the assembler  reads  the  source  files  and
     defines all symbols used.  All illegal characters read will cause
     a diagnostic to be printed.  If any symbols remain undefined, the
     undefined  address  diagnostic is printed with the address of the
     first occurrence of the symbol.

          During PASS 2, the assembler  reads  the  source  files  and
     generates  the  binary code using the symbol table defined during
     PASS 1.  The binary file consists of leader,  an  initial  origin
     setting  of  200, datawords, origins and field settings generated
     from the source files,  and  is  terminated  by  a  checksum  and
     trailer.  This file may be punched on paper tape etc, for loading
     using the PDP-8 Binary  Loader.   An  illegal  reference  may  be
     diagnosed  during PASS 2.  If the ASR-33 is being used for binary
     output, the diagnostic will be both printed and punched but  will
     be  preceded  and followed by a <RUBOUT>.  The Binary Loader will
     ignore everything on the files between the rubouts.

          During PASS 3, the assembler  reads  the  source  files  and
     generates  the code from the source statements.  Each line of the
     listing file contains the current location counter, the generated
     code  in  octal  and  the  source statement.  The symbol table is
     printed at the end of the pass, if requested.





































  PAL8XR X-ASSEMBLER                                          Page   6



  8.  ERROR MESSAGES

  a) I/O error messages

     CSI-F-Device full -- No room on output device, consult the  RT-11
             System   User's  Guide  for  the  appropriate  corrective
             action.  (e.g.   'squeeze'  the  existing  files  on  the
             device, select another device etc).

     CSI-F-File not found        ) Check command for syntax and
     CSI-F-Illegal command       ) spelling errors. If OK, take
     CSI-F-Illegal device        ) appropriate action.

     CSI - F - INVALID SWITCH OPT -- A switch other than /S or /F  was
             used.  Re-enter the command string.

     READ ERR CHAN # -- Hard error occurred on  input.   (Input  files
             are  assigned  to  channels  3 to 8 in the order of their
             occurrence in the CSI command string).  Fatal error.

     WRITE FAILED CHAN # -- Hard error  occurred  on  output.   Binary
             file  is  assigned  to  channel  0  and  the  listing  to
             channel 1.  Fatal error.

     NO PROG TERMINATOR  --  All  the  input  data  was  read  without
             encountering  a  program  terminator  ('$'),  or no input
             files were specified in the CSI  command  string.   Fatal
             error.


  b) Assembly error messages

     The assembly errors have the following form:

                  XX   YYYY(YY)   AT  ZZZZ

     Where XX is the error type
     YYYY(YY) is the octal code or ASCII label in error, and
     ZZZZ the location in the user's program where the error occurred.

     The following error types can occur:

     ST - Symbol Table overflow.  More symbols have been defined  than
          there  is  room  in core for.  The YYYY value is meaningless
          with this printout.   No  recovery  is  possible  from  this
          error.    The   user  program  must  be  re-written  or  the
          cross-assembler re-assembled with a larger symbol table.

     IC - Illegal character used as a delimeter.  The  YYYY  value  is
          the octal value of the bad character.

     IR - Illegal reference.  An indirect  reference  was  made  to  a
          symbol that is not on the current page.  A link could not be
          generated for this word because the indirect bit has already
          been set.







  PAL8XR X-ASSEMBLER                                          Page   7



     RD - Redefinition of a permanent symbol.  A permanent  symbol  is
          being redefined using an equate (parameter) assignment.  The
          ZZZZ value is the new value of the symbol.

     DT - Duplicate Tag.  the same symbol is being defined again using
          a direct assignment.  The new value is ignored.

     UA - Undefined Address (symbol).  Reported  after  PASS  1.   The
          symbol is automatically redefined to a 7402 (HLT).

     The assembler errors are generally printed during PASS 1, but  an
     'IR' will be reported during PASS 2.


  9.  PDP-11 REGISTER USAGE

     R0 - temporary storage for the character to be output;  used  for
          argument  transmission  during  calls  to  the  PDP-11 MACRO
          library.

     R1 - pointer to next character to be fetched from input buffer

     R2 - temporary storage for an ASCII character  fetched  from  the
          input buffer; used as linkage to one subroutine.

     R3 - 

     R4 - general register.

     R5 - general register, and used for subroutine linkage.

     R6 - stack pointer.

     R7 - program counter.