DECUS C LANGUAGE SYSTEM


                                The AS Assembler
                                 for the PDP-11


                                       by

                                David G.  Conroy


                                    Edited by

                                  Martin Minow




        This  document  describes  the AS assembler, used to compile the
        output of the Decus C compiler to PDP-11 object code.  




                         DECUS Structured Languages SIG

                             Version of 11-Nov-1983


                                      NOTE

             This  software  is  made available without any support
             whatsoever.    The   person   responsible    for    an
             implementation of this system should expect to have to
             understand and modify the source code if any  problems
             are  encountered  in  implementing  or maintaining the
             compiler  or  its   run-time   library.    The   DECUS
             'Structured  Languages  Special Interest Group' is the
             primary focus for communication among  users  of  this
             software.  



        UNIX  is  a  trademark  of  Bell  Telephone  Laboratories.  RSX,
        RSTS/E, RT-11  and  VMS  are  trademarks  of  Digital  Equipment
        Corporation.  


        AS Reference Manual                                               Page 3



        1.0  Introduction              ____________

        AS  is a three pass assembler for the PDP-11 intended for use as
        a target assembler for compilers.  It lacks  some  of  the  more
        esoteric  assembler  directives  of the standard DEC assemblers;
        it also lacks any form of  macro  facility.   However,  it  does
        posess  the  ability  to  extend any branch instruction which is
        unable to reach its target label  into  the  appropriate  branch
        over a jump.  

        The  input  syntax is, in general, similar in style to MACRO-11.
        The actual details have in many cases been  changed  so  that  a
        program  intended  to  be  assembled with AS cannot be assembled
        with MACRO-11.  The  syntax  is  compatible  with  the  Unix  AS
        assembler.  


        2.0  Usage              _____

        Under   RSX-11M,  RSX  compatibility  mode  under  VMS,  or  RSX
        compatiblity mode under RSTS/E, AS is invoked as follows:  

                XAS file [file ...] [-options] 

        or      RUN XAS         AS> file [file ...] [-options] 

        Under  RT-11  compatibility  mode under RSTS/E, AS is invoked as
        follows:  

                AS file,file=file[/options] 

        Under RT-11, AS is invoked as follows:  

                RUN AS 
                AS> object,list=source[/options] 

        In  RSX  mode,  the specified files are assembled separately and
        the object code is placed in a file (on the same device  and  in
        the same UIC) having the same name as the source file but with a
        filetype of OBJ.  The default filetype for source files  is  .S.
        Wildcard  file names are permitted on native RSX-11M and RSX-11M
        compatibility mode under VMS.  They are not permitted on  RSTS/E
        or RT-11.  

        In RT-11 mode, only one file may be assembled and the object and
        list files may be explicitly named.  The default case:  

                AS file 

        is equivalent to 

                AS file=file 

        The following options are defined:  

        AS Reference Manual                                               Page 4




            b   Causes  the  assembler  to  flag  all branches that were
                extended to jumps.  

            d   Causes  the  assembler  to  delete the source file after
                assembly.  This option makes compiling C  programs  much
                easier.  This option is turned off by errors.  

            g   Causes  all  symbols  which  are undefined at the end of
                pass 1 to be given the type  undefined  external;   this
                corresponds to the .ENABL GBL directive of MACRO-11.  

            l   Causes  the  assembler to generate a listing file.  This
                is the only way to generate a listing file on RSX  mode.
                It works on RT-11 mode as well.  

            n   Causes  the  assembler  to produce no object file.  This
                option is primarily used to prevent creating  a  lot  of
                useless  object  files  when  debugging  the  assembler;
                however, it may be of use  when  one  wishes  to  simply
                check a file for errors.  

            s   Causes  the  assembler to write internal symbol records.
                These are needed to support  symbolic  debuggers.   Note
                that,  since,  the  Decus  C  compiler does not generate
                internal symbol tables,  the  assembler  symbol  records
                will  only  contain  global  data  and  function  names.
                Statement  numbers,  local  variables,   and   structure
                offsets are not available.  

        The  object  file  is in standard DEC format.  Note that the RSX
        compiler produces an object  file  in  the  format  required  by
        TKB.TSK, while the RT-11 compiler produces an object file in the
        format required by LINK.SAV.  

        The  title  of  the  object  file is always set to the first six
        characters of the source file name.  This is of interest only to
        people who load overlaid programs off libraries.  


        3.0  Lexical Conventions              _______ ___________

        Assembler  tokens  consist  of identifiers ('symbols', 'names'),
        constants and operators.  


        3.1  Identifiers              ___________

        An  identifier consists of a sequence of alphanumeric characters
        (including the period '.', the tilde  '~',  and  the  underscore
        '_'),  the  first  of  which may not be numeric.  Only the first
        eight characters of the name  are  significant;   the  rest  are
        discarded.   Upper  and  lower  case  are  treated  identically.
        Because the DEC object file stores symbols in radix 50, the  '_'

        AS Reference Manual                                               Page 5



        character  is  mapped  to  '.' in the symbol table while the '~'
        character is mapped to  '$'.   Global  symbols  must  be  unique
        within the first six characters.  If a global symbol begins with
        an underscore '_', it will  be  stripped  off.   This  allows  C
        programs  to  use PDP-11 register names, such as "sp", in global
        symbols as the compiler will preface all global symbols  with  a
        '_'.  


                                     WARNING

             Note  that  the  mapping of '_' to '.' and the magical
             properties  of  '_'  in  global   symbols   constitute
             incompatible  changes  from  earlier  versions of this
             assembler.  




        3.2  Constants              _________

        An  octal  constant  is  a  sequence of digits;  '8' and '9' are
        taken to have  octal  values  of  10  and  11.   The  number  is
        truncated  to  16  bits  and  interpreted  in  two's  complement
        notation.  

        A  decimal  constant  is  a  sequence  of digits terminated by a
        period.  The magnitude of the constant should  be  representable
        in 15 bits;  i.e., be less than 32,768.  

        A  single  character constant consists of the single quote (''')
        followed by any  ASCII  character  (except  the  newline).   The
        constant's  value  is the code for the character right justified
        in the word, with zeros on the left.  


        3.3  Operators              _________

        There  are several single and multiple character operators;  see
        section 6.1.  


        3.4  Blanks and Tabs              ______ ___ ____

        Blanks  and  tabs may be used freely between tokens, but may not
        appear within identifiers.  A blank or  a  tab  is  required  to
        separate adjacent tokens not otherwise separated.  


        3.5  Comments              ________

        The  character  '/'  introduces a comment, which continues until
        the end of line.  Comments are ignored by the assembler.  

        AS Reference Manual                                               Page 6



        4.0  Program Sections              _______ ________

        AS  permits  multiple  program  sections  (PSECTS).  The default
        attributes are LOW, NOLIB, CON, RW, REL, LCL and ISPACE.  Option
        bytes  may  be  specified to allow attribute specification shown
        below.  


        5.0  The Location Counter              ___ ________ _______

        The  special  symbol  '.' is the location counter.  Its value is
        the offset into the current program section of the start of  the
        statement  in which it appears.  It may be assigned to, with the
        restrictions that the assignment  must  not  either  change  the
        program section or cause the value to decrease.  


        6.0  Statements              __________

        A  program  consists  of  a  sequence of statements separated by
        newline or semicolons.  There are  three  kinds  of  statements;
        null statements, assignment statements and keyword statements.  

        Any statement may be preceeded by any number of labels.  


        6.1  Labels              ______

        A  name  label  consists  of  an  identifier followed by a colon
        (':').  The program section and value of the label  are  set  to
        those  of the location counter.  It is an error for the value of
        a label to change between pass 1 and pass2.  

        A  temporary  label consists of a digit '0' to '9' followed by a
        colon (':').  Such a label serves to define temporary symbols of
        the  form  'xf'  and  'xb', where 'x' is the digit of the label.
        References of the form 'xf' refer to the first  temporary  label
        'x:'  forward  from the reference;  those of the form 'xb' refer
        to the first temporary label 'x:' backward from  the  reference.
        Such  labels tend to conserve both the symbol table space of the
        assembler and the inventive powers of the programmer.  


        6.2  Null Statements              ____ __________

        A  null  statement  is just an empty line (which may have labels
        and be followed by a comment).  Null statements are  ignored  by
        the  assembler.   Common  examples  of null statements are empty
        lines or lines consisting of only a label.  

        AS Reference Manual                                               Page 7



        6.3  Assignment Statements              __________ __________

        An assignment statement consists of an identifier followed by an
        equal sign ('=') and  an  expression.   The  value  and  program
        section  of  the  identifier  are set to that of the expression.
        Any symbol defined by an assignment statement may be  redefined,
        either by another assignment statement or by a label.  


        6.4  Expression Statements              __________ __________

        An expression statement consists of an arithmetic expression not
        beginning with a keyword.  The assembler computes its  (16  bit)
        value  and  places  it  in  the  output  stream  along  with the
        appropriate relocation.  


        6.5  String Statements              ______ __________

        A  (UNIX  style)  string statement generates a sequence of bytes
        containing ASCII characters.  It consists of a left string quote
        '<'  followed  by  a  sequence of ASCII characters not including
        newline followed by a  right  string  quote  '>'.   Any  of  the
        characters may be replaced by an escape sequence as follows:  

                \b      Backspace       (0010)
                \f      Formfeed        (0014)
                \n      Newline         (0012)
                \r      Carriage Return (0015)
                \t      Tab             (0011)
                \nnn    Octal value     (0nnn)

        These escape sequences may also be used in the .ASCII and .ASCIZ
        keyword statements and in character constants.  


        6.6  Keyword Statements              _______ __________

        Keyword statements are the most common type;  all of the machine
        operations and assembler pseudo operations are of this type.   A
        keyword  statement begins with one of the assembler's predefined
        keywords, followed by any operands  required  by  that  keyword.
        All of the keywords and their required operands are described in
        sections 7 and 8.  


        7.0  Expressions              ___________

        An  expression is a sequence of symbols representing a value and
        a program section.  Expressions  are  made  up  of  identifiers,
        constants,  operators  and  brackets.  All binary operators have
        equal precidence and are executed in  a  strict  left  to  right
        order (unless altered by brackets).  

        AS Reference Manual                                               Page 8



        7.1  Types              _____

        Every  expression  has  a  type determined by its operands.  The
        types that will be met explicitly are:  


            Undefined 

                Upon  first  encounter,  each  symbol  is  undefined.  A
                symbol may also become undefined if it is assigned to an
                undefined  expression.   It  is  an error to assemble an
                undefined expression in pass 2.  Pass 1 allows  assembly
                of undefined expressions, but phase errors may result if
                undefined  expressions  are  used  in  certain  contexts
                (i.e., in a .BLKW or .BLKB).  


            Absolute 

                An  absolute  symbol  is  one  defined ultimately from a
                constant or  from  the  difference  of  two  relocatable
                values.  


            Register 

                Register  symbols  refer to the general registers of the
                PDP-11.   They  are  required  to  distinguish  register
                addressing  from  normal memory addressing.  The symbols
                R0, R1, R2, R3, R4, R5, SP  and  PC  are  predefined  as
                register symbols.  


            Relocatable 

                All  other  user symbols are relocatable symbols in some
                program section.  Each program section  is  a  different
                relocatable type.  

        Each keyword in the assembler has a secret type which identifies
        it internally.  However, all of these secret types are converted
        to  absolute in expressions.  Thus any keyword may be used in an
        expression to obtain the  basic  value  of  that  keyword.   For
        machine operations the basic value is the opcode with all of the
        addressing  bits  set  to  zero;   the  basic  value  of  pseudo
        operations is, in general, uninteresting.  


        7.2  Operators              _________

        The operators are:  

                '+'             Addition
                '-'             Subtraction

        AS Reference Manual                                               Page 9



                '*'             Multiplication
                '%'             Integer (truncating) division
                '&'             Bitwise AND
                '|'             Bitwise OR
                '>>'            Arithmetic right shift
                '<<'            Arithmetic left shift
                '-'             Unary negation
                '!'             Unary ones complement
                '^'             Value of the left, type of the right

        Expressions  may be grouped by means of square brackets ('[' and
        ']');  parentheses are reserved for use in address expressions. 


        7.3  Type Propagation in Expressions              ____ ___________ __ ___________

        When  operands are combined in expressions the resulting type is
        a function of both the types of the operands and  the  operator.
        Only   the   '+'   and   binary  '-'  operators  can  manipulate
        non-absolute operands.  

        The  '+'  operand  permits the addition of two absolute operands
        (yielding an absolute result) and the addition of an absolute to
        a  non-absolute operand (yielding a result with the same type as
        the non-absolute operand).  As a consequence, R3 may be  refered
        to as R0+3.  

        The  binary  '-' operator permits two operands of the same type,
        including relocatable, to be subtracted  (yielding  an  absolute
        result)  and  an  absolute  to be subtracted from a non-absolute
        (yielding a result with  the  same  type  as  the  non  absolute
        operand).  

        The notion of 'complex relocation' is not supported.  


        8.0  Pseudo Operations              ______ __________

        The  keywords  listed  below introduce statements which generate
        data or effect the later operation of the assembler.  


        8.1  .BYTE expression [ , expression ] ...               _____ __________ _ _ __________ _ ___

        The  expressions  in the comma separated list are truncated to 8
        bits and are assembled into successive bytes.   The  expressions
        must be absolute.  


        8.2  .WORD expression [ , expression ] ...               _____ __________ _ _ __________ _ ___

        The  expressions  in the comma separated list are assembled into
        successive words.  

        AS Reference Manual                                              Page 10



        8.3  .ASCII string              ______ ______

        The  first  nonblank (or tab) character after the .ASCII keyword
        is taken as a delimiter.  Successive characters from the  string
        are  assembled  into  successive  bytes  until  the delimiter is
        encountered.  


        8.4  .ASCIZ string              ______ ______

        This  pseudo  operation  is  identical  to .ASCII except that it
        appends a null byte to the end of the string.  


        8.5  .IDENT string              ______ ______

        The  first  nonblank (or tab) character after the .IDENT keyword
        is taken as a delimiter.  Successive characters from the  string
        (which  must  follow  Radix-50 conventions) are assembled into a
        module identifier until the delimiter is encountered.  Only  the
        first  six  bytes  will  be recognized.  Shorter strings will be
        left-justified.  The .IDENT field provides a way of recording  a
        program  version  number in the object module;  it has no effect
        on the computation.  


        8.6  .EVEN              _____

        If  the  location counter is odd, output a null byte so the next
        statement will be assembled on an even boundry.  


        8.7  .ODD              ____

        If  the  location  counter is even, assemble a null byte so that
        the next statement will be assembled on an odd boundry.  


        8.8  .BLKB expression              _____ __________

        This  statement  assembles  into  expression  null  bytes.   The
        expression must be absolute.  


        8.9  .BLKW expression              _____ __________

        This  statement  assembles  into  expression  null  words.   The
        expression must be absolute.  

        AS Reference Manual                                              Page 11



        8.10  .GLOBL identifier [ , identifier ] ...                ______ __________ _ _ __________ _ ___

        The  identifiers  in  the  comma  separated  list  are marked as
        global.  If they are defined in the current assembly they may be
        referenced  by other object modules;  if they are undefined they
        must be resolved by the loader before execution.  


        8.11  .ENTRY expresion               ______ _________

        The  value of the expression becomes the transfer address of the
        object file.  This provides the function of  the  label  on  the
        .END statement in MACRO-11.  


        8.12  .PSECT identifier               ______ __________

        This  statement  switches the assembler to the specified program
        section.  If  the  program  section  has  not  been  encountered
        previously  '.' is set to 0;  otherwise it is set to the highest
        location already assembled into that  program  section.   .PSECT
        attributes can be specified as follows:  
                d Data space
                i Instruction space (default)
                r Read-only
                w Read-write (default)
                g Global scope
                l Local scope (default)
                o Overlay
                c Concatenate (default)


        8.13  .LIMIT               ______

        This  statement assembles into two words that are filled in with
        program limit information by the linker.  When  the  program  is
        executed,  the  first  word  will have the lowest address in the
        load image and the second word will have the highest address  in
        the load image.  


        8.14  .FLT2     number [ , number ] ...                _____     ______ _ _ ______ _ ___

        The  floating  point  numbers  in  the  comma separated list are
        converted to single precision  floating  point  binary  and  are
        assembled into successive two word blocks.  


        8.15  .FLT4     number [ , number ] ...                _____     ______ _ _ ______ _ ___

        The  floating  point  numbers  in  the  comma separated list are
        converted to double precision  floating  point  binary  and  are
        assembled into successive four word blocks.  

        AS Reference Manual                                              Page 12



        8.16  End of file               ___ __ ____

        The  assembly source is terminated by the end of the input file.
        There is no separate .END statement.  


        9.0  Machine Instructions              _______ ____________

        Because  of  the  rather  complicated instruction and addressing
        structure of the PDP-11, the syntax of the machine  instructions
        is  varied.   The  PDP-11  handbooks should be consulted for the
        detailed semantics of the instructions.  


        9.1  Sources and Destinations              _______ ___ ____________

        The  syntax  of  general source and destination addresses is the
        same as in MACRO-11, except that '$' has  been  substituted  for
        '#' and '*' has been substituted for '@'.  


        9.2  Simple Machine Instructions              ______ _______ ____________

        The following simple machine instructions are defined:  

                HALT                    WAIT
                RTI                     BPT
                IOT                     RESET
                RTT                     CLC
                CLV                     CLZ
                CLN                     SEC
                SEV                     SEZ
                SEN                     CLE     (= CLC)
                SEE     (= SEC)

        The  PDP-11  hardware  allows  more  than  one  of the 'set' and
        'clear' instructions to be ored together.  There is no syntactic
        provision for this;  such instructions may be generated by means
        of the .WORD pseudo operation.  


        9.3  Branches              ________

        The  following  instructions  take  an expression as an operand.
        The expression must lie in the same program section as '.'.   If
        the value of the expression differs from the current location by
        more than 254 (decimal) bytes the  instruction  assembles  as  a
        branch   to   .+6   having  the  opposite  sense  to  the  coded
        instruction, followed by a jump to the desired location.  

                BR                      BNE
                BEQ                     BPL
                BMI                     BVS
                BVC                     BCS

        AS Reference Manual                                              Page 13



                BCC                     BES     (= BCS)
                BEC     (= BCC)         BLT
                BGT                     BGE
                BLE                     BHI
                BLOS                    BHIS
                BLO 


        9.4  Single Operand Instructions              ______ _______ ____________

        The  following  single  operand instructions take one address of
        the general source-destination type.  

                CLR                     CLRB
                COM                     COMB
                INC                     INCB
                DEC                     DECB
                NEG                     NEGB
                TST                     TSTB
                ASR                     ASRB
                ASL                     ASLB
                ROR                     RORB
                ROL                     ROLB
                ADC                     ADCB
                SBC                     SBCB
                JMP                     SWAB
                SXT


        9.5  Double Operand Instructions              ______ _______ ____________

        The    double    operand    instructions    take   two   general
        source-destination type address fields, separated by a comma.  

                MOV                     MOVB
                CMP                     CMPB
                BIT                     BITB
                BIS                     BISB
                BIC                     BICB
                ADD                     SUB


        9.6  Other Instructions              _____ ____________

        The following instructions have a more specialised syntax.  Here
        reg  specifies  a  register  expression,  src  and  dst  general
        source-destination addresses, and expr an expression.  

                JSR     reg,dst 
                RTS     reg
                CALL    dst             (same as JSR PC,dst)
                CALLR   dst             (same as JMP dst)
                RETURN                  (same as RTS PC)
                EMT     expr

        AS Reference Manual                                              Page 14



                TRAP    expr
                SYS     expr            (same as EMT expr)
                ASH     src,reg
                ASHC    src,reg
                MUL     src,reg
                DIV     src,reg
                XOR     reg,dst
                MARK    expr
                SOB     reg,expr

        The  expression  in a SOB must be in the same program section as
        '.' and must be within 176 bytes of '.'.  The assembler does not
        attempt  to  adjust  SOB's which cannot reach their destinations
        into DEC and BNE, because  the  DEC  and  BNE  do  not  set  the
        condition codes in the same manner.  


        9.7  Floating Point Instructions              ________ _____ ____________

        The  following  floating  point  instructions  are defined, with
        syntax as indicated.  

                ABSF    dst             ABSD    dst
                ADDF    src,reg         ADDD    src,reg
                CLRF    dst             CLRD    dst
                CMPF    reg,dst         CMPD    reg,dst
                DIVF    src,reg         DIVD    src,reg
                LDCDF   src,reg         LDCFD   src,reg
                LDCIF   src,reg         LDCID   src,reg
                LDCLF   src,reg         LDCLD   src,reg
                LDEXP   src             LDFPS   src
                LDF     src,reg         LDD     src,reg
                MODF    src,reg         MODD    src,reg
                MULF    src,reg         MULD    src,reg
                NEGF    dst             NEGD    dst
                STCFD   reg,dst         STCDF   reg,dst
                STCFI   reg,dst         STCDI   reg,dst
                STCFL   reg,dst         STCDL   reg,dst
                STEXP   dst             STFPS   dst
                STF     reg,dst         STD     reg,dst
                SUBF    src,reg         SUBD    src,reg
                SETF                    SETD
                SETI                    SETL
                STST    dst             CFCC
                TSTF    dst             TSTD    dst


        10.0  Diagnostics               ___________

        Syntactic  or  semantic  errors  in  the  source are reported by
        displaying the offending line on the console  device,  preceeded
        by  the  appropriate  error flags.  The name of the file is also
        displayed.  


        AS Reference Manual                                              Page 15



                a               Addressing
                b               Byte allignment
                d               Illegal operation on '.'
                e               Expression syntax
                j               Jump (-b)
                m               Multiple definition
                o               Illegal operation code
                p               Phase
                q               Questionable syntax
                r               Relocation
                u               Undefined symbol

        Errors  encountered  in  the  accessing  of files or in internal
        assembler operations are reported  in  English  on  the  console
        device.   Overflows  are fatal and require that the assembler be
        modified to have a larger table (this is easy).  

        The  only  really  cryptic diagnostic is 'AS>', which means that
        the MCR command line could not be obtained (you  probably  typed
        RUN  AS).   Type  the  command  line you would have typed at MCR
        (including the leading AS).  


        11.0  Installation Notes               ____________ _____

        The  AS  assembler may be installed on RSTS/E (V7.0 or later) in
        RSX or RT-11 modes, on RSX-11M (V3.2 or later), on RT-11 (V3B or
        later),  or  on  VMS  compatiblity  mode.  This section contains
        installation instructions for RSTS/E and VMS.  


        11.1  Installation on RSTS/E               ____________ __ ______

        The  AS assembler is installed after building the CC compiler as
        it must refer to the compiler support  library  which  is  built
        together with CC.  Assuming the AS modules are stored in account
        [5,3], the following command files should be run by ATPK:  

                XMAKAS          Make RSX-style assembler 
                RMAKAS          Make RT-11 style assembler 

        You will have to edit the various command files as needed.  

        In order to use AS, the System Manager must add the following to
        the startup command file:  

                RUN $UTILTY
                ADD LOGICAL [5,2] C
                CCL XAS-=C:AS.TSK;0
                CCL AS-=C:AS.SAV;8192
                EXIT

        AS Reference Manual                                              Page 16



        11.2  Installation on VMS               ____________ __ ___

        The  build  command  file  for  the  AS assembler is VMAKAS.COM,
        located in the same directory as other compiler components.  You
        will  have  to  edit  it  as  needed,  running it as an indirect
        command file.  

        To use the assembler, define it as a command as follows:  

                XAS :== $device:[account]AS.EXE XAS 


        11.3  Installation on RT-11               ____________ __ _____

        After  building  the  CC  compiler,  the TMAKAS.COM command file
        should be edited and executed.  


        11.4  Installation on RSX-11M               ____________ __ _______

        After  building  the  CC  compiler,  the MMAKAS.CMD command file
        should be invoked.