DECUS C LANGUAGE SYSTEM


                               Compiler & Library
                             Software Support Manual


                                       by

                                  Martin Minow


                                    Edited by

                                Robert B.  Denny



        This  document describes the RSX/POS/VMS/RSTS/RT11 DECUS C lang-
        uage system runtime support library.  It also contains  all  in-
        ternal  functions  and  such compiler internal information as is
        available.  


                         DECUS Structured Languages SIG

                             Version of 28-July-1984


                                      NOTE

             This  software  is  made available without any support
             whatsoever.    The   person   responsible    for    an
             implementation of this system should expect to have to
             understand and modify the source code if any  problems
             are  encountered  in  implementing  or maintaining the
             compiler  or  its   run-time   library.    The   DECUS
             'Structured  Languages  Special Interest Group' is the
             primary focus for communication among  users  of  this
             software.  



        UNIX  is  a  trademark  of  Bell  Telephone  Laboratories.  RSX,
        RSTS/E,  RT11  and  VMS  are  trademarks  of  Digital  Equipment
        Corporation.  














                                    CHAPTER 1

                                  INTRODUCTION



        The C support library contains three major groups of functions: 

             o  Functions  called  by  the  compiler  to perform certain
                mathematical operations (such as floating-point multiply
                or function entrance) that are not performed in-line.  

             o  Functions  that  may  be called by C programs to perform
                operations, such as copying  a  string,  that  are  more
                efficiently  performed  by  optimized  assembly language
                subroutines.  

             o  An  implementation  of  (most  of) the Unix Standard I/O
                library.  

        The  standard  installation procedure yields two documents.  The
        Runtime Support Library Reference Manual describes  how  to  use
        the C library.  The Compiler and Library Software Support Manual
        contains all user documentation plus additional  information  on
        the  internals  of both the library and the C compiler.  This is
        the Software Support Manual.  

        This release is the first to support the RMS-11(V2) file system.
        The runtime library may optionally be built to use RMS.  If this
        is  done, the advantages are compatibility across DECnet between
        RSX, POS and VMS systems, and  transparent  remote  DECnet  file
        access.   RMS  is  the preferred system for use on MICRO-RSX and
        P/OS.  













                                    CHAPTER 2

                              THE STANDARD LIBRARY



        This  manual  describes  the DECUS C "standard I/O" package.  It
        was developed with the idea of maintaining maximum compatibility
        with  the  UNIX  Version  7  environment and maximum portability
        between Digital operating systems.  

        This  release (28-July-1984) of the library can be built for use
        on RSX-11 (and  friends)  and  P/OS  to  use  either  FCS-11  or
        RMS-11(V2) record I/O systems.  FCS-11 is the traditional record
        I/O package used on RSX and the RSTS/RSX emulator.  In the  last
        several  years, however, the RMS-11 system has undergone a major
        overhaul, the result of which is  a  very  complete,  reasonably
        fast record I/O package.  

        P/OS   (the   Professional  300  series  operating  system)  and
        MICRO-RSX are oriented toward RMS-11.  Both systems are  shipped
        with the RMS resident shared library (called RMSRES) genned into
        the system.  You might as well use it if you can afford the loss
        of  8K words (2 APR's) of virtual address space.  It is possible
        to use RMS without RMSRES but your task  image  will  be  larger
        than it would if you used FCS.  


                                      NOTE

             The  RMSRES  shared  library is "vectored".  What this
             means is that the entry points are  kept  in  a  fixed
             table  at  the base of the region, and their locations
             are guaranteed not to change with successive  releases
             of RMS.  So you can build tasks against RMSRES without
             the worry that the task will fail if  the  library  is
             revised.  One other bit of trivia ...  RMSRES on P/OS,
             MICRO-RSX, RSX-11M and M-PLUS and,  yes,  even  RSTS/E
             (V8 & later) have IDENTICAL vectoring.  


        The  native  RSX library build command file MMAKLB.COM gives you
        the choice of building the FCS or RMS flavors of the library.  

        All  C  programs  should  be  linked  together with the run-time
        support  library.   On  systems  that  support  logical   device

[[        C Compiler and Library]]                                      Page 2-2
        Software Support Manual


        descriptors,  this  will  generally be stored in the C:  logical
        device/account.  On  RSX-11M,  the  library  will  be  found  in
        LB:[1,1].   On  PRO/Toolkit  (native  P/OS)  the library will be
        found in LB:[1,5].  To link a C program, proceed as follows:  

        RSX (FCS flavor):
            LINK/CHECK/OPT/EXE:task objects+LB:[1,x]C/LIB

        RSX/POS (RMSRES flavor):
            LINK/CHECK/OPT/EXE:task objects+LB:[1,x]C/LIB
            Option? STACK=1024
            Option? LIBR=RMSRES:RO
            Option?

        RT11 & TSX+
            R LINK
            *save,map=objects,C:SUPORT,C:CLIB/B:2000
            *^C

        Note  that, on RSX-11M, the task should be built checkpointable.
        This is automatic on RSTS/E and VMS emulated modes.   On  native
        RSX-11M, the task-builder may be rebuilt with /CHECKPOINT as the
        default.  If the /CHECKPOINT option is not given, the  task  may
        abort  (no  memory)  when started.  Stack extension is needed if
        subroutines locally allocate large amounts of data or if  RMSRES
        is  in use.  The easiest way to handle this is to make a command
        file for linking.  

        On  RT11,  note  that  the '/B' (bottom) switch must be given to
        increase the size of the run-time  stack.   This  is  needed  as
        local  variables  are allocated on the stack.  If the stack size
        is not increased,  the  program  may  abort  without  any  error
        message.  

        The  standard  I/O  interface  header  file  is in C:STDIO.H, or
        LB:[1,1]STDIO.H  on  native  RSX-11  or  LB:[ZZDECUSC]  on   POS
        PRO/Toolkit,  and  should  be  included  in  all  C  programs as
        follows:  

                        #include <stdio.h> 


                                     WARNING

             If  you  are  using the RMS flavor of the standard I/O
             package,  there  is  an  alternate  header  file  that
             describes  the  modified  "iov" for RMS.  It is called
             RMSTDIO.H.  Programs which make use  of  the  "secret"
             fields  in  the  iov  must  use RMSTDIO.H.  Otherwise,
             STDIO.H is fine.  



[[        C Compiler and Library]]                                      Page 2-3
        Software Support Manual


        2.1  Introduction to Unix-style Stream I/O              ____________ __ __________ ______ ___


        This   section  presents  an  overview  of  the  'standard'  I/O
        interface for C programs.  These routines have  proven  easy  to
        use and, while they do not provide the full functionality of RSX
        or RMS, they give the programer essentially all that  is  needed
        for everyday use.  The discussion includes the following:  

                - Opening and closing files
                - Reading data from files
                - Writing data to files
                - Interaction with host operating system
                - DECnet considerations (RMS only)

        Note  that  this  file  system is limited:  files are sequential
        with only a limited amount of random-access  capability.   Also,
        little of the power of RMS/FCS is available.  On the other hand,
        the limitations make C programs easily  transportable  to  other
        operating systems.  

        When  a  C  program  is  started, three files are predefined and
        opened:  

                stdin    The 'standard' input file 
                stdout   The 'standard' output file 
                stderr   The 'standard' error file 

        Stderr  is  always  assigned to the command terminal.  Stdin and
        stdout are normally assigned to the command terminal, but may be
        reassigned or closed when the program starts.  


        2.2  Opening and Closing Files              _______ ___ _______ _____

        The  fopen  and  fclose functions control access to files.  They
        are normally used as follows:  

                #include <stdio.h>      /* Define standard I/O  */
                FILE    *ioptr;         /* Pointer to file area */
                ...
                if ((ioptr = fopen("filename", "mode")) == NULL)
                        error("Can't open file");

        All  information  about an open file is stored in a buffer whose
        address is returned  by  fopen().   The  buffer  is  dynamically
        allocated  when the file is opened and deallocated when the file
        is closed.  Its format is described under the heading IOV.   The
        mode  string  contains  flags  defining  how  the  file is to be
        accessed:  

                r       Read only
                w       Write new file
                a       Append to existing file (or write new)

[[        C Compiler and Library]]                                      Page 2-4
        Software Support Manual


                        (Doesn't work on RT11 modes).

        It also defines some record-control information:

                n       No newlines mode ('binary' files)
                u       RSX:  The user program allocates record buffers
                        RT11: Console output is done using .ttyout

        If  mode 'n' is specified, the RSX I/O routines do not interpret
        the end of a RMS  logical  record  as  defining  the  end  of  a
        human-readable  line.   This  is  necessary  to process 'binary'
        information.   On  RT11,  the  I/O  routines   do   not   remove
        carriage-returns   from   input   files,   nor  do  they  insert
        carriage-returns when newlines are output.  

        Mode  'u'  is treated differently on RSX and RT11.  If specified
        on RSX the user maintains the file's record buffer.  The program
        may  only  call  the fget() and fput() routines.  Each such call
        will be translated directly to an RMS/FCS  GET$  or  PUT$  call.
        (In  RT11 mode, fput() may be used to write binary records which
        are subsequently read by fget().  The file should be opened with
        'n' mode.) 

        If  mode  'u' is specified on RT11 mode when opening the console
        terminal, single character output will be performed  (using  the
        RT11 monitor routine .ttyout).  If not specified, output will be
        one line at a time (using  the  monitor  routine  .print).   The
        library  initialization  process  opens  stderr  in mode 'u' and
        stdout in normal mode.  This means that mixing I/O to both units
        will    result   in   synchronization   problems.    To   obtain
        single-character output  on  stdout,  the  program  need  simply
        execute:  

                if (freopen("tt:", "wu", stdout) == NULL) error("");  


        The  program  calls  fclose(ioptr)  to terminate processing on a
        file.  This  closes  the  file  and  reclaims  system-controlled
        buffer space.  fmkdl(ioptr) may be called to close and delete an
        open file.  


        2.3  Reading Data from a File              _______ ____ ____ _ ____

        The  simplest  way  to  read  a file is to call the getchar() or
        getc() routines which read the next character from a file.   For
        example,  the  following program counts the number of characters
        in a file:  

                #include <stdio.h>
                main()
                {
                        register int    ccount;
                        register int    lcount;

[[        C Compiler and Library]]                                      Page 2-5
        Software Support Manual


                        register int    c;
                        FILE            *ioptr;
                        if ((ioptr = fopen("foo.bar", "r")) == NULL)
                                error("Cannot open file");
                        ccount = 0;
                        lcount = 0;
                        while ((c = getc(ioptr)) != EOF) {
                                ccount++;
                                if (c == '\n') lcount++;
                        }
                        printf("%d characters, %d lines.\n",
                                        ccount, lcount);
                }

        Other input routines include:  

                gets    Read a line from the standard input
                fgets   Read a line from a file
                fgetss  Read a line from a file, remove terminator
                ungetc  Push one character back on a file
                fseek   Position the file to a specific record

        These  routines  are  used  together  with the ferr() and feof()
        functions  which  allow  testing  for  error  and  end  of  file
        conditions,  respectively.   The  package assumes that all error
        conditions are lethal and force end of file.  


        2.4  Writing Data to a File              _______ ____ __ _ ____

        There  are  several  routines for data output which are directly
        analagous to the data input routines:  

                putchar Write a character to standard output
                putc    Write a character to a specified file
                puts    Write a string to the standard outpt
                fputs   Write a string to a specified file
                fputss  Write a record to a specified file
                ftell   Return record location (for fseek)

        In addition, the printf() or fprintf() routine is used to format
        and print data (as was shown in the previous example).  Printf()
        is  flexible,  powerful,  and  easy  to use;  and is perhaps the
        single most important routine in the file system.  


        2.5  Interaction with the Operating System              ___________ ____ ___ _________ ______

        The  support  library attempts to provide a consistant operating
        system interface on several implementations of  quite  different
        operating  systems  and  in  some cases two different record I/O
        packages (FCS and RMS).  The possiblities include:  

            Operating systems:  

[[        C Compiler and Library]]                                      Page 2-6
        Software Support Manual



             o  Native RT11 

             o  Native RSX-11M, RSX-11M PLUS, IAS and MICRO-RSX 

             o  P/OS (Professional 350 operating system) 

             o  RT11    emulated on RSTS/E 

             o  RSX-11M emulated on RSTS/E 

             o  RSX-11M emulated on VAX/VMS 

            Record I/O systems (RSX, RSTS, P/OS) 

             o  Native FCS-11 (RSX and friends) 

             o  FCS-11 emulated on RSTS/E(RSX) 

             o  Native RMS-11 (RSX, P/OS, RSTS/E(RSX)) 

        This  section  mentions the inconsistencies and random bugs that
        are more or less intentionally present.  


        2.5.1  Logical Unit Numbers                _______ ____ _______


        RT11,  RSTS/E,  and RSX-11M use small integers to number all I/O
        channels.  Unfortunately, the numbering is  not  consistent  and
        channel  usage  differs  among  the  various  systems.  This has
        resulted in several quirks:  

             o  On  RT11,  console terminal interaction uses the .ttyout
                and .print monitor functions.  While no device is opened
                by the fopen() function, a channel number is reserved.  

             o  On  RSX-11M,  a channel must be allocated to the console
                terminal.   When  a  C  program  starts,  the   'command
                terminal'  is  opened  on logical unit 1 and assigned to
                stderr.  This is not  done  using  the  fopen()  routine
                (although  the  stderr  IOV  structure  is defined as if
                fopen()  were  called).   Also,  fclose()  cannot  close
                stderr.  

                In  addition to the standard I/O routines, there are two
                routines, msg() and  regdmp(),  that  direct  output  to
                logical  unit  1.  These routines were used to debug the
                library, and are otherwise  useful  for  disasters.   On
                RT11,   msg()   and  regdmp()  use  the  .print  monitor
                function.  

             o  On  both  systems,  the  first  true files are stdin and
                stdout.  These are opened  on  logical  units  0  and  1

[[        C Compiler and Library]]                                      Page 2-7
        Software Support Manual


                (RT11) or 2 and 3 (RSX).  Code in fclose() double-checks
                that the logical unit number of the  file  being  closed
                corresponds  to  the  proper  slot  in  the logical unit
                table.  

             o  Since  the  standard  I/O routines know little about the
                operating system, they do not deal with certain  special
                features.  

                For  example,  on RT11, the 'user service routine' (USR)
                is used to open files.  The file open routine  does  not
                attempt  to  locate  IOV  areas so that the USR does not
                swap over them.  This can be a problem  for  very  large
                programs.  

                On  RSX,  logical unit numbers are assigned dynamically.
                This means that  'LUN  assignment'  cannot  be  reliably
                performed   by   task-build   control   files  (or  task
                initiation).  


        2.5.2  File and Directory Names                ____ ___ _________ _____


        Unfortunately,  each  operating system has its own way of naming
        files and directories.  Programs  written  with  portability  in
        mind  should  NOT make assumptions about the format or structure
        of file names.  


        2.5.3  Wild-Card Files                _________ _____


        The  fwild()  and  fnext()  routines  can  be  used  to  process
        'wild-card' files.  

        On  RSX-11M  and  VMS/RSX  emulation,  the file name, extension,
        and/or  file  version  may  be  expressed  as  '*'  to  indicate
        wild-card  support.   Due to restrictions in the RSX-11 Files-11
        structure (ODS1), the ' ', ';0' and ';-1' version  numbers  will
        NOT function properly on native RSX-11.  This means that '*.MAC'
        will not work, for instance.  The algorithm in  fwild()  depends
        on  the  directory  being  sorted, as in the ODS2 file structure
        used on VAX/VMS.  If you sort the directory to  be  used  in  an
        fwild() operation (use the SRD program available from DECUS with
        the /WB switch) in order of  decreasing  file  version  numbers,
        then the " ", ";0", and ";-1" versions will work.  

        With  FCS,  wild-card  devices,  units,  directory names, or UIC
        codes are not supported.  With RMS, wildcard directory names and
        UIC's are allowed, except with remote (DECnet) files.  Note that
        VMS V4 may support RMS-11(V2) under the (optional) AME.  

        Note  that,  on  RSX11  emulated  on  VMS,  the  ';-1' (earliest

[[        C Compiler and Library]]                                      Page 2-8
        Software Support Manual


        version) requires special processing by  the  user  program,  as
        noted in the description of fwild().  

        On  RSX-11M  emulated  on RSTS/E, the file name and/or extension
        may contain '*' or '?' wild-cards.  Wild-card devices, units, or
        UIC (PPN) codes are not supported.  

        On RT-11, the file name and/or extension may contain '*', '%' or
        '?' wild cards.  The  '?'  wild-card  is  synonymous  with  '%'.
        Wild-card  devices, or units are not supported.  Since wild-card
        support is not an RT-11 system service, the  file  specification
        parsing  and  directory  operations are handled by the C library
        fwild() and fnext() functions.  The fwild/fnext module  requires
        about  480  words  of storage.  Also, a file opened by wild-card
        uses a 1024 byte buffer, twice the normal size, which is  shared
        between data and directory operations.  


        2.5.4  DECnet Remote File Access                ______ ______ ____ ______


        If  you  are  using the RMS version of the standard I/O library,
        your applications automatically have access to files  on  remote
        nodes  on  DECnet.   As is the case on the VAX (RMS-32), the new
        RMS-11 provides transparent DECnet  (DAP)  remote  file  access.
        What  this  means  to  you  is  that you can develop distributed
        applications in DECUS C  if  you  use  the  RMS  flavor  of  the
        library.   This  is  true  of both RSX & friends and RSTS/E.  If
        your network consists of a mixture of host types, such as VAXen,
        RSTS  and  RSX  systems,  remote  file  access can give you some
        surprises.  Most of the  quirks  are  listed  in  your  system's
        DECnet "Cross System Notes".  

        On RSX and P/OS, the DECnet remote file capability presents some
        interesting capabilities.  For example, you may give full remote
        file  specifications  on the command line when redirecting stdin
        and stdout:  

            $ FOO
            TT2> <NODE1"USER PSWD"::USER_ROOT:[DIR.SUB]FILE.EXT

        The  above  would connect program FOO's "stdin" stream to a file
        on a remote VAX/VMS system  named  "NODE1".   Note  that  RMS-11
        accepts  a  full  VMS-style  hidden  device  and  tree directory
        specification.  The default device and  directory  (if  none  is
        explicitly supplied) is that of "USER" on the VAX whose password
        is "PASSWORD".  Note that the VMS filespec redirection  was  not
        given  on  the  FOO  command  line.   Getting  foreign filespecs
        through DCL requires some quote-mark  hacking,  but  it  can  be
        done.  For example:  

            $ FOO <"NODE1""USER PSWD"""::"USER_ROOT:[DIR.SUB]FILE.EXT"
        but this is easier:
            $ FOO <NODE1/USER/PSWD::"USER_ROOT:[DIR.SUB]FILE.EXT"

[[        C Compiler and Library]]                                      Page 2-9
        Software Support Manual


                                      NOTE

             Someone should try building the RMS library for RSTS/E
             emulator.  It is supposed to work.  




        2.5.5  Memory allocation                ______ __________


        Memory  is  allocated  using  the  malloc()  function.  It works
        correctly on all operating systems, expanding memory on RSX  and
        RT11/RSTS.   On 'native' RT11, all available memory is allocated
        by invoking the monitor .settop function with a  '-2'  argument.
        Neither library supports extended memory (PLAS) directives.  

        The  sbreak()  routine  may  be used for permanent allocation of
        memory.  Once memory  has  been  allocated  using  sbreak(),  it
        cannot be freed.  

        If  you  are using the RMS flavor of the I/O library and linking
        with RMSRES, you may notice that your task image is smaller than
        an  FCS version would be.  RMS allocates all buffers and control
        blocks dynamically.  This means that your program will expand at
        run  time  more than an FCS version.  Keep this in mind ...  RMS
        tasks require quite a bit more dynamic memory then FCS ones.  


        2.5.6  Global symbols                ______ _______

        Global  symbols  defined  or  referenced by C programs may cause
        unexpected parts of the operating-system support library  to  be
        loaded,   with  undesirable  consequences.   There  are  several
        aspects to this problem:  

             o  A symbol refered to by a C program which is not resolved
                by the object modules or libraries may cause  some  part
                of the system library to be loaded.  For example, if a C
                program refers to the  sqrt()  function  (which  is  not
                present in the standard library), the linker may attempt
                to load the function from the  Fortran  library.   Since
                the  Fortran sqrt() function contains a reference to the
                Fortran run-time error message routine, the load map may
                contain many strange global symbols.  

             o  Another problem occurs when a C program defines a global
                symbol that duplicates a global in the  system  library.
                This  may  prevent  loading  some  necessary part of the
                system library, causing the link to fail with unresolved
                global  symbols.   For  example,  on RSX-11M emulated on
                RSTS/E V7.0, the following will fail:  

                        int eof;        /* Global       */

[[        C Compiler and Library]]                                     Page 2-10
        Software Support Manual


                        main () {
                        }














                                    CHAPTER 3

                               SUPPORT INFORMATION



        The  C  system  has  been implemented on VMS V3.4, RSX-11M V4.1,
        P/OS V1.7 and V2.0 with PRO/Toolkits V1.7 and V2.0, RSTS/E V8.0,
        and  RT11 V5.  All installations should expect to have to modify
        the command procedures to suit their specific needs.  While  the
        compiler  has  been  built  from scratch on RT11, the procedures
        unrealistically  assume  a   system   with   no   disk   storage
        limitations.   The C system has not been tested on IAS, RSX11-D,
        or HT11.  



                                   Please Note

             This  is  a  DECUS  'product';   there  is  no support
             available from the authors.   The  person  responsible
             for  an implementation of this system should expect to
             have to understand and modify the source code  if  any
             problems    are   encountered   in   implementing   or
             maintaining the compiler or its run-time library.  The
             DECUS 'Structured Languages Special Interest Group' is
             the primary focus for  communication  among  users  of
             this software.  


        This  section  contains  information  on  the  internals  of the
        compiler,  assembler,  and  run-time  libraries.   It   is   not
        complete;  it is probably not accurate either.  


        3.1  The C Compiler              ___ _ ________

        The  compiler source is distributed on account [5,3].  There are
        four groups of files in this account:  

             o  The  C  compiler  source  is in modules named CC???.MAC.
                The root code is in CC0RT.MAC,  while  overlays  are  in
                CC00?.MAC,  CC10?,  CC20?, and CC3??.  The overlays have
                the following functions:  

                 0. Pass  0  reads  the  input  source  file,  writing a

[[        C Compiler and Library]]                                      Page 3-2
        Software Support Manual


                    temporary file after processing  #define,  #include,
                    and #ifdef statements.  

                 1. Pass  1  reads  the expanded source file, parses the
                    language and writes an 'intermediate code' file.  In
                    the  intermediate  file  all  operations  have  been
                    converted into 'low-level' constructions.   Variable
                    and  structure references are compiled into absolute
                    expressions.  All information  needed  by  the  code
                    generator  is  contained  in  this file.  Except for
                    compiler flags and file names, nothing  is  retained
                    in memory.  

                 2. Pass  2 reads the code file, writing PDP-11 assembly
                    language  (in  the  format  requested  by   the   AS
                    assembler).  

                 3. Pass  3  contains  some  end  of  processing code to
                    delete work files.  

                All  internal  files are in Ascii.  In order to make the
                compiler portable between RSX,  RSTS/E,  and  RT11,  the
                file  system  is simple and inefficient.  RT11 users may
                run into intermediate  file  size  problems.   The  only
                (software)  solution  requires  invoking the compilation
                with explicit size arguments for the output files:  

                        #out.s[N1],interm.tm1[N2],expand.tmp[N3]=in.c 

                The expanded source file should be less than the size of
                the  input  file   plus   all   #include   files.    The
                intermediate  file size may be as much as twice the size
                of the expanded source file.  

             o  C  programs are assembled into PDP-11 object code by the
                AS assembler, whose source files are named 'AS????.MAC'.
                The AS assembler is described in AS.DOC.  

             o  A support library for the two compilers is included in a
                group of files labeled A?????.MAC.  The C compiler build
                process  also  builds the support library.  This library
                is similar -- but  not  identical  --  to  the  run-time
                support library.  

        The  compiler  and  assembler are installed by executing command
        files.  There are several groups of command  files  supplied  to
        assist  in  implementation on the various operating systems.  It
        is highly likely that the files will have to be edited  to  suit
        each  individual installation's needs.  VMS, RSX, and RT11 files
        are run by the indirect command  file  processor,  while  RSTS/E
        files  are  run by the ATPK system program.  RSTS/E installation
        requires must be run from a privileged account.  

        The  following  file  conventions  are  used:  VMS command files

[[        C Compiler and Library]]                                      Page 3-3
        Software Support Manual


        begin with the letter 'V', RSTS/E RT11 mode with the letter 'R',
        and  RSTS/E  RSX  mode with the letter 'X'.  Native RT11 command
        files begin with 'T' and native RSX-11M  files  begin  with  the
        letter  'M'.  Thus, XMAKCC.CMD builds the CC compiler for RSTS/E
        RSX-11M mode.  The '.TKB' files are indirect command  files  for
        the task-builder.  


                                     Warning

             As  distributed,  the  compiler and run-time libraries
             assume hardware  support  for  the  SXT  (sign-extend)
             instruction.  This is present on all PDP-11 CPU's with
             EIS, and on all versions of the LSI-11 (11/03, LSI-11,
             11/23).  If the compiler is to generate code that will
             run on the 11/04, 11/05, 11/10, 11/20, or on an  11/40
             without  EIS;   all RSX.MAC and RT11.MAC configuration
             files must be edited to define symbol C$$SXT equal  to
             zero.   Note  that  the  compiler  must  be build with
             C$$SXT set correctly.  

             As  distributed,  the  RSX  configuration files assume
             hardware  EIS  support.   If  this  is  not  the  case
             (hardware  EIS  is  not  needed  for RSX-11M) edit the
             RSX.MAC control files to define symbol C$$EIS equal to
             zero.  There are two RT11 configuration files, and the
             RSTS/E library build procedure builds an EIS  library,
             CLIB.OBJ,  as  well  as a library without EIS support,
             CLIBN.OBJ.  

             The  default  'native'  RT11  command  file  builds  a
             non-EIS library, naming it CLIB.OBJ.  Programs  linked
             against  the non-EIS library will run on machines with
             EIS.  Also, save-images linked on  RT11  will  run  on
             RSTS/E and vice-versa without relinking.  

             There  are  certain  differences  in task-image format
             between native RSX-11M  and  RSX-11M  as  emulated  on
             RSTS/E.    Thus,  only  source  or  object  files  are
             transportable between the two operating systems.  




        3.2  The C Run-time Support Library              ___ _ ________ _______ _______

        The  C support library is distributed on two accounts, [5,4] and
        [5,5].  Account [5,4] contains only those routines which have no
        I/O  dependencies, while account [5,5] contains the standard I/O
        library.  

        Many  routines  are conditionally compiled to select RT11 or RSX
        mode.  All routines should  be  compiled  together  with  either
        RT11.MAC  (no  EIS support), RT11.EIS (hardware EIS support), or

[[        C Compiler and Library]]                                      Page 3-4
        Software Support Manual


        RSX.MAC, identical copies of which are present in each account. 

        To  build  the  libraries,  execute one of the following command
        files:  

                RMAKLB.CMD      RT11 library on RSTS/E
                VMAKLB.COM      RSX  library on VMS
                XMAKLB.CMD      RSX  library on RSTS/E
                MMAKLB.CMD      RSX  library on RSX-11 (RMS or FCS)
                TMAKLB.COM      RT11 library on RT11

        Account  [5,1]  contains  a  program, GETCMD.C which was used to
        build assembler command  files.   On  RSTS/E,  a  command  file,
        [5,1]RLBCMD.CMD,  may  be  used  to  rebuild all library command
        files.  

        All library source code is in PDP-11 MACRO.  


        3.3  The RSTS/E Interface Library              ___ ______ _________ _______

        Account  [5,6]  contains  a  library of subroutines that allow C
        programs access to all RSTS/E executive functionality.  There is
        no documentation other than the source code and [5,6]README.506. 


        3.4  The RSX-11 + P/OS Extensions Library              ___ ______ ______ __________ _______

        Account  [5,7]  contains  a  library of subroutines that allow C
        programs access to all RSX-11M, M+, MICRO-RSX and P/OS executive
        functionality,  including  AST's.  Refer to [5,7]CX.DOC for more
        information.  This library has not  been  tested  on  'emulated'
        RSX-11M modes (under VMS or RSTS/E), nor on IAS.  

        This  library  may  be  built on any of the RSX-ish systems, but
        several services are particular  to  certain  systems.   The  CX
        build command file CXMAK.CMD allows you to build the library for
        native  use  on  RSX-11M,  RSX-11M  PLUS,  MICRO-RSX   or   P/OS
        PRO/Toolkit.   In  addition, it may be build on RSX for use with
        the Host Toolkit for P/OS.  In the latter case, the library will
        be specially named and placed in LB:[1,5], the toolkit UIC.  See
        [5,7]CXMAK.CMD for more information.  


        3.5  RT11 Extensions Library              ____ __________ _______

        Access to RT11 executive functionality may be had by calling the
        system library (SYSLIB).  The C library call()  routine  may  be
        used  to  generate  the  necessary calling sequences.  Note that
        SYSLIB routines that depend on Fortran I/O conventions must  not
        be called.  

[[        C Compiler and Library]]                                      Page 3-5
        Software Support Manual


        3.6  C Tools and Toys              _ _____ ___ ____

        The  distribution  kit  contains  several  accounts [6,*] with C
        programs and subroutines.  Account [6,1] contains a  library  of
        'software tools' which should be useful for all C installations.
        Among these are the following:  

                echo    Echo  arguments  onto the standard output.  This
                        program  serves  as  the  primary  test  of  the
                        run-time library.  

                grep    'Get  regular  expression pattern.' This program
                        reads one or more  files,  printing  text  lines
                        that match a given pattern.  

                kwik    'Key word in context' utility.  

                sortc   A file sort utility.  

                sorts   Sort-merge  subroutines  for  incorporation into
                        other programs.  

                wc      Count  bytes,  words,  and  lines in one or more
                        files.  

                ccxrf   Cross-referenced listings for C source files.  

        Please  refer  to  README.???  files in the appropriate accounts
        for more information.  


        3.7  Building the Documentation              ________ ___ _____________

        Compiler  and  assembler  documentation  is in CC.RNO and AS.RNO
        respectivly.  These files, stored in [5,1]  or  [.COMMAND],  are
        compiled  into  .DOC  files  by using Runoff.  The documentation
        build control file appends the current problem list CBUGS.RNO to
        CC.RNO before building the documentation.  


                                      NOTE

             In  order  to  create titles properly on VMS "Standard
             Runoff," a command line is present which may  cause  a
             non-fatal   error  message  to  be  printed  by  other
             versions  of  Runoff,  notably  RNO.TSK.   This  error
             message should be ignored.  



        The  source  of the library documentation is included within the
        library source (Macro) files.  

        To  build the library documentation, the following programs must

[[        C Compiler and Library]]                                      Page 3-6
        Software Support Manual


        have been built and installed on the system:  

                getrno  This  program  reads  the  library  header file,
                        breaking out wizard and non-wizard sections.  It
                        then reads a set of macro files (specified using
                        a wild-card convention).  Each file contains its
                        own  documentation  in  the  form of commentary.
                        This  follows  a  specific,  rigid   format   as
                        described in the documentation of getrno.c.  

                        The  output  of  getrno  is a runoff source file
                        which is then merged with the various appendices
                        to the library documentation.  

                        The  source  of  getrno.c  is stored in [5,1] or
                        [.COMMAND].  The  running  program  is  normally
                        stored in C:.  

                getkwk  This  program  reads  the  library  macro files,
                        searching   for   "Index"   entries    in    the
                        documentation.   The  output of getkwk is passed
                        directly to kwik.  

                        The  source  of  getkwk.c  is stored in [5,1] or
                        [.COMMAND].  The  running  program  is  normally
                        stored in C:.  

                kwik    This  is the keyword in context program which is
                        used to build the library index.  It is built as
                        part of the tools build procedure.  

                        The  source  of  kwik.c  is  stored  in [6,1] or
                        [.TOOLS].   The  running  program  is  generally
                        written  to  a  public library, PUB:  on RSTS/E,
                        BIN:  on VMS.  

                fixdoc  On  RSTS/E  RNO.TSK  and  VMS "Standard RUNOFF",
                        page numbers are put at the "page right  margin"
                        (column  80)  instead  of the text right margin,
                        column 72.  As a workaround, getrno is  used  to
                        mark runoff .title lines.  Fixdoc is then run to
                        straighten out the titles.  Note  that  this  is
                        needed for RSTS/E RNO and VMS RUNOFF only.  

                        The  source  of  fixdoc.c  is stored in [5,1] or
                        [.COMMAND].  The  running  program  is  noramlly
                        stored  in  C:.   Note  that  is is used only on                                                                 ____
                        RSTS/E.  

        The control files [5,1]RGTRNO.CMD and [5,1]RGTDOC.CMD illustrate
                        the  process  on  RSTS/E  while  VGTRNO.COM  and
                        VGTDOC.COM illustrate it on VMS.  













                                    CHAPTER 4

                          COMPILER INTERNAL INFORMATION



        As noted above, compiler work files are in human-readable Ascii.
        The  parser  generates  a  temporary  file  with   an   internal
        pseudo-code.   The  code  generator converts this pseudo-code to
        PDP-11  assembly  language.   Except  for  compiler  flags,  all
        communication between passes is via intermediate files.  


        4.1  Intermediate Code File Format              ____________ ____ ____ ______

        The  intermediate  code file consists of single line entries for
        each operation.  The first byte  is  an  operator,  followed  by
        parameter  entries as needed.  Numeric values are transmitted in
        octal.  The following operators are defined:  

            Location counter control:
                C               Switch to the string  P-section (c$strn)
                O               Switch to the data    P-section (c$data)
                P               Switch to the program P-section (c$code)
                Ux[name] [attr] Define program section (x == P or D)

            Flow control:
                L [number]      Define a local label
                J [number]      Jump to a local label
                X               Function exit
                N               Function entry

            Data reservation, etc.:
                A               Generate a  .even pseudo-op
                B [number]      Generate a  .blkb [number]
                D               Generate an external label
                G               Generate a  .globl
                H               Generate a  .byte
                I               Generate a  .word as a local pointer
                Y               Generate a  .word

            Special operations:
                @               No-op: generate a comment
                W               Generate a switch table
                Q               Dump symbol table entry (-t switch)
                M               Transmit a line number between passes

[[        C Compiler and Library]]                                      Page 4-2
        Software Support Manual



            Tree (expression) operators:
                R               Return
                S               Switch
                E               Compile for effect
                T               Jump if true
                F               Jump if false
                K               Initialize variable
                Z               Tree item

        Note  that 'trees' are the result of compiling expressions, such
        as 

                (a + b * (c & 4)) * d 

        Each  non-terminal  node  of a tree generally consists of a left
        part, an operation, and a right part.  Operator  precedence  has
        been resolved.  The above example thus becomes:  

                              |
                      ------------------
                      |                |
                  ---------            |
                  |       |            |
                  |    --------        |
                  |    |      |        |
                  |    |    -----      |
                  |    |    |   |      |
                ((a + (b * (c & 4))) * d)

        Trees   are   described  by  'Z'  records.   Tree  elements  are
        variable-length records, the first value describing the operator
        (and,  hence,  the  length).   All numeric values are encoded as
        octal ascii strings.  The tree types are as follows:  

        OP.EOF  Used to signal a null tree element.  

        OP.CON  Constant, followed by 4 values.  

        OP.REG  Register, followed by type and register number.  

        OP.INX  Offset from register, followed by type, register number,
                and offset value.  

        OP.ID   Global  identifier,  followed  by  type,  and identifier
                name.  

        OP.LID  Local identifier (label), followed by number.  

        other   An  operator  (OP.ADD,  etc.) followed by the type code.
                Subsequent records contain the left  subtree,  then  the
                right  subtree.   (OP.EOF  is  used  to  signal  a  null
                subtree.) 


[[        C Compiler and Library]]                                      Page 4-3
        Software Support Manual


        For  example,  here  is a simple subroutine and the intermediate
        code it generates (the trees have been compressed):  

                fact(n)         D fact          | define function fact
                {               N 0 4           | enter function
                  if (n == 0)   F 1             | if false, goto L1
                                Z [n == 0]      | compile expr. value
                    return(1);  R               | return
                                Z [1]           | compile expr. value
                                J 2             | goto L2
                  return(n * fact(n - 1));
                                L 1             | Label L1, N != 0
                                R               | return
                                Z [n * fact(n - 1)]
                                                | compile expr. value
                                L 2             | label L2
                }               X               | Exit from function
                                G fact          | .globl fact

        The  C  source  code  is parsed by a top-down, recursive parser.
        Expressions are parsed bottom-up, by priority.  Casts  of  types
        are  processed  by  special  routines.   The  parser  does  some
        optimizations, such as constant folding.   Also,  all  automatic
        variables  (local  to a function), are assigned absolute offsets
        from the argument frame (Register 5), while  structure  elements
        are assigned absolute offsets from the base of the structure.  


        4.2  The Code Generator              ___ ____ _________

        The  code  generator  consists of a top-level input file reader,
        which processes 'easy things' directly.  It calls subroutines to
        compile  switch  statements  and  expressions.   The  expression
        compiler performs various optimizations,  calls  a  Sethi-Ullman
        register  allocator,  then  a  code generator.  The Sethi-Ullman
        algorithm was described in the Journal of the  ACM,  Volume  17,
        No.  4, October 1970.  pp.  715-728.  


        4.2.1  Optimizations and Register Allocation                _____________ ___ ________ __________


        The following optimizations are performed:  

             o  Expressions are reordered.  

             o  Constant expressions are folded.  

             o  Dummy operations are eliminated, including -(-A), !(!A),
                ~(~A), (A & A) and (A | A).  

             o  Dummy  address  expressions  are  eliminated:  *(&A) and
                &(*A) all become A.  


[[        C Compiler and Library]]                                      Page 4-4
        Software Support Manual


             o  Constant  address arithmetic is performed in expressions
                such as &A + const.  

             o  Constant  offsets from registers become index operations
                in expressions such as *(reg  +  constant)  or  *(reg  -
                constant).  

             o  PDP11   autoincrement  and  autodecrement  are  used  in
                expressions such as *p++ and *--p.  

             o  Conversion  between  integer  and  pointer datatypes are
                converted to multiply and divide operations.  

             o  Multiply by 1 is deleted.  

             o  The and operator is converted to BIC.  

             o  Null  operations are deleted, including +0, -0, &-1, |0,
                ^0, |=0, etc.  

             o  If  the  compiler  has  been  built for in-line floating
                point (i.e., the machine  on  which  the  compiler  runs
                supports  floating  point), floating point constants are
                folded.  

        Register allocation is as follows:  

             o  R0 and R1 are always scratch registers.  

             o  R2, R3, and R4 may be reserved by the C program by using
                the 'register ...' construction.  The parser  tells  the
                coder  the  highest register it can use (in the function
                initialization intermediate code operation).  

             o  The   Sethi-Ullman   algorithm   stores  the  number  of
                registers needed into each tree node.   This  number  is
                always  >=  2 to insure that R0 and R1 are available for
                scratch usage.  

             o  'A  tree  is  easy  if  the  other  tree uses few enough
                registers and there is a free register available.' 

             o  The  GETREG  subroutine  claims  registers.  If the code
                table is modified, be sure that GETREG isn't called on a
                tree that isn't easy.  


        4.2.2  Code generation                ____ __________


        Almost all code is generated by expanding macro operators out of
        the code tables.  There are four tables (CTAB, ETAB, STAB, RTAB)
        and  a  pseudo-table,  TTAB.   Only  RTAB  is  complete,  If  an
        expansion which was attempted in  CTAB  or  ETAB  fails,  it  is

[[        C Compiler and Library]]                                      Page 4-5
        Software Support Manual


        retried  in RTAB followed by a test (CTAB), move (ETAB), or push
        (STAB) operation.   For  example,  if  an  expansion  which  was
        attempted in STAB fails, it is done by:  

                [Rtab] 
                mov     Reg,-(sp) 

        The  code  body is in Ascii;  bytes with the parity (eighth) bit
        set are used macro operators:  'address of left', 'push  right',
        etc.  

        Code  table  entries  are  selected by the type of the arguments
        (int, char, long, unsigned, float, double, and pointer)  and  by
        kind (constant, address, easy, and any).  

        Here is a typical code table (for addition):  

                int     any     int     con1    ; Add 1 to any integer
                        [LL]                    ; Compile left (subtree)
                        inc     [R]             ; INC Rx

                int     any     int     addr    ; Add var. to anything
                        [LL]                    ; Compile left (subtree)
                        add     [AR],[R]        ; ADD var,Rx

                int     any     int     easy
                        [SRV]                   ; Setup right value,
                                                ; NOP if it's an address
                        [LL]                    ; Compile left (subtree)
                        add     [AR],[R]        ; Add var,Rx

                int     any     int     any
                        [PR]                    ; Compile right to stack
                        [LL]                    ; Compile left to reg.
                        add     (sp)+,[R]       ; ADD (sp)+,Rx

        Here is another example, '= for effect' (as in 'A = B;'):  

                int     any     int     con0    ; I = 0;
                char    any     int     con0    ; C = 0;
                        [SLAC]                  ; Get left op. address
                        clr[TL] [AL]            ; CLR(B) var

                int     addr    int     any
                char    addr    int     any
                        [LR]                    ; Compile right subtree
                        mov[TL] [R],[AL]        ; MOV(B) Rx,var

                int     any     int     easy
                char    any     int     easy
                        [SRV]                   ; Setup right value
                        [SLAC]                  ; Setup left address
                        mov[TL] [AR], [AL]


[[        C Compiler and Library]]                                      Page 4-6
        Software Support Manual


                int     any     int     any
                char    any     int     any
                        [PLA]                   ; Push left address
                        [LR]                    ; Compile right value
                        mov[TL] [R],@(sp)+

        Note  that  the  "easy"  storage will handle indirect addressing
        "(rx)", as well  as  autoincrement  "@(rx)+"  and  autodecrement
        "@-(rx)".   If  the  datum  is  long,  the  <ALN> and <ARN> code
        operators perform the address computation without  side-effects.
        For example, the following computation performs "i <<= 8", where
        'i' is an integer:  

                        swab    [ALN]
                        clrb    [ALN]
                        mov     [AL],[R]


        4.2.3  Macros used in code generation                ______ ____ __ ____ __________


        The following are defined in the code generator:  

                [M]     Set modulo return
                [F]     Set function return
                [F.1]   Result value is in r1
                [R]     Current register
                [R.1]   Current register + 1
                [AL]    Address of left
                [AL.2]  Address of left+2 (long int)
                [AL.4]  Address of left+4, double
                [AL.6]  Address of left+6, double
                [ALN]   Address of left, no side effect
                [AR]    Address of right
                [AR.2]  Address of right, long
                [ARN]   Address of right, no side effect
                [OP.0]  Opcode
                [OP.1]  Opcode
                [TL]    Type of left
                [T]     Type of right or left
                [SRVA]  Set right value anywhere
                [SRV]   Set right value
                [SRAA]  Set right address anywhere
                [SRA]   Set right address
                [SLVA]  Set left value anywhere
                [SLV]   Set left value
                [SLAA]  Set left address anywhere
                [SLA]   Set left address
                [SLAC]  Set left address current reg.
                [LL]    Load left
                [LL.1]  Load left into [R+1]
                [LL.O]  Load left into odd register
                [LLP.O] Load left into odd of pair of registers
                [LLP.E] Load left into even of pair or registers

[[        C Compiler and Library]]                                      Page 4-7
        Software Support Manual


                [LR]    Load right
                [LRP.E] Load right into even of pair of registers
                [PL]    Push left
                [PLA]   Push left address
                [PR]    Push right
                [V]     ADC or SBC for longs
                [FPI]   Set floating point to I mode
                [FPL]   Set floating point to L mode
                [FPF]   Set floating point to single precision
                [FPD]   Set floating point to double precision
                [GO.TO] Branch within code table
                [IFEIS] Compile if hardware EIS support
                [IFFPU] Compile if hardware FPU support
                [IFOP]  Compile if specifed opcode
                [ELSE]  Compile if IF... test was false
                [ENDIF] End IF... block
                [DEBUG] Write debug record to .S file














                                    CHAPTER 5

                          LIBRARY FUNCTION DESCRIPTIONS



        This  chapter  contains  descriptions  of each of the C-callable
        runtime  library  functions.   In  addition,   descriptions   of
        internal routines are provided.  

        In  most cases the I/O functions match those of UNIX V7 closely,
        with differences normally called  out.   For  more  information,
        consult  "The  C  Programming  Language"  by Brian Kernighan and
        Dennis   Ritchie   (Englewood   Cliffs,   NJ:     Prentice-Hall,
        ISBN 0-13-110163-3).  

        Routines  and  global  symbols  beginning with '$$' are used for
        communication among the I/O routines.  Routines whose names  are
        of  the form 'ABC$X' implement the 'ABC' instruction for the 'X'
        data type.  For example, 'ASL$LI' implements an arithmetic  left
        shift of a long value by an integer argument.  

[[        C Compiler and Library]]                                      Page 5-2
        $$abuf  Allocate memory for i/o buffers


        5.1  Allocate memory for i/o buffers              ________ ______ ___ ___ _______



                                   **********
                                   * $$abuf *
                                   **********



        File name:      ioabuf.mac


        Usage

                mov     #iov,r4 ;file data block
                call    $$abuf  ;Allocate it
                bcs     error   ;Exit on errors

        Description

                A block of memory is allocated.  If it succeeds, the iov
                record buffer is correctly setup and $$abuf returns  the
                buffer  address  in  r0.   If it fails, an error code is
                stored in $$ferr, the error bit  set  in  the  iov  flag
                word,  r0 is set to 0, and $$abuf returns with the C-bit
                set.  

                In  RSX mode, the record gets padding that may be needed
                by $$put.  

        Bugs 


[[        C Compiler and Library]]                                      Page 5-3
        $$c5ta  Convert Radix-50 to Ascii


        5.2  Convert Radix-50 to Ascii              _______ ________ __ _____



                                   **********
                                   * $$c5ta *
                                   **********



        File name:      c5ta.mac


        Usage

                mov     rad50_word, r1
                mov     out_ptr, r0
                call    $$c5ta

                Return:
                        r0 updated
                        r1 random
                        other registers preserved.

        Description:

                Convert  one  radix-50  word  to three Ascii bytes.  All
                letters will be in upper-case.  The output  buffer  will
                not be null-trailed, nor will blank fields be supressed. 

        Bugs 


[[        C Compiler and Library]]                                      Page 5-4
        $$cl16  Close all channels


        5.3  Close all channels              _____ ___ ________



                                   **********
                                   * $$cl16 *
                                   **********



        File name:      iocl16.mac


        Usage

                $$cl16();               /* Close all channels   */

        Description

                This  module  closes  all I/O channels.  It is called on
                exit from C programs.  

        Diagnostics 

        Bugs 


[[        C Compiler and Library]]                                      Page 5-5
        $$clfu  Flush last record before closing


        5.4  Flush last record before closing              _____ ____ ______ ______ _______



                                   **********
                                   * $$clfu *
                                   **********



        File name:      ioclfu.mac


        Usage

                mov     #iov,r4         ;r4 -> i/o vector
                call    $$cflu          ;Flush buffers for close

        Description

                Flush  the output buffer if the file is open for output.
                On RSX, the code may be conditionally compiled  so  that
                the last buffer is fixed so it is SEE compatible.  

        Bugs 


[[        C Compiler and Library]]                                      Page 5-6
        $$ctim  Convert $$rtim Buffer to Ascii


        5.5  Convert $$rtim Buffer to Ascii              _______ ______ ______ __ _____



                                   **********
                                   * $$ctim *
                                   **********



        File name:      rctime.mac


        Usage

                char *
                $$ctim(buffer);
                struct TIME {
                        int     year;   /* G.TIYR  year - 1900  */
                        int     month;  /* G.TIMO  Jan. = 1     */
                        int     day;    /* G.TIDA               */
                        int     hour;   /* G.TIHR  00 .. 23     */
                        int     minute; /* G.TIMI  00 .. 59     */
                        int     second; /* G.TISC  00 .. 59     */
                        int     tick;   /* G.TICT  00 .. tsec-1 */
                        int     tsec;   /* G.TICP  tick/second  */
                } buffer;

                dayofweek(buffer);
                struct TIME buffer;

        Description

                $$ctim() converts the time information in buffer such as
                returned by  $$rtim()  to  a  character  string  in  the
                format:  

                        Sun Sep 16 01:03:52 1973\0\0

                All the fields have constant width.  Note that there are
                two  trailing  <null>'s  for  the  benefit  of  programs
                converted  from  Unix  (where  the year is followed by a
                <newline>).  

                $$ctim(0)  returns  the  current  time  of  day, calling
                $$rtim() internally.  

                The  format  of the returned information is identical to
                the Unix function of the same name except that the  Unix
                function has a trailing newline which is omitted here.  

                dayofweek() returns the day of the week (Sunday = 0) for
                the date information in the argument buffer.  


[[        C Compiler and Library]]                                      Page 5-7
        $$ctim  Convert $$rtim Buffer to Ascii


        Bugs 

                There is no range checking on the information passed.  


[[        C Compiler and Library]]                                      Page 5-8
        $$div2  Unsigned divide (Macro only)


        5.6  Unsigned divide (Macro only)              ________ ______ ______ _____



                                   **********
                                   * $$div2 *
                                   **********



        File name:      div2.mac


        Usage

                mov     hi_div,r0       ;High-order dividend
                mov     lo_div,r1       ;Low-order  dividend
                mov     divisor,r2      ;Divisor
                jsr     pc,$$div2       ;Perform the division
                mov     r0,hi_quotient  ;High-order quotient
                mov     r1,lo_quotient  ;Low-order  quotient
                mov     r2,remainder    ;Remainder


        Description

                Perform  an unsigned double-precision division.  This is
                needed for one of the library conversion routines.  

        Bugs 


[[        C Compiler and Library]]                                      Page 5-9
        $$dtoa  Convert floating to ASCII


        5.7  Convert floating to ASCII              _______ ________ __ _____



                                   **********
                                   * $$dtoa *
                                   **********



        File name:      dtoa.mac


        Usage

                char *
                $$dtoa(buff, conv, field, dplace, value)
                char    *buff;          /* Where it goes        */
                char    conv;           /* Conversion type      */
                int     field;          /* Maximum field width  */
                int     dplace;         /* Decimal part width   */
                double  value;          /* What to convert      */

        Description

                $$dtoa()  is  called  to  do the conversion to Ascii The
                text is written to buff[].  $$dtoa() returns  a  pointer
                to the trailing null byte.  

                Field  and  dplace are the conversion parameters "f" and
                "d" in the format string "%f.df".  Conv is 'e', 'f',  or
                'g'  to  define  the  format.   Note that the conversion
                character must be in lower-case.  

                $$dtoa()    is   called   by   printf   to   convert   a
                double-precision value to Ascii.  The text is written to
                buff[].   Field and dplace are the conversion parameters
                "f" and "d" in the format string "%f.df"  Conv  is  'e',
                'f', or 'g' to define the format.  Note:  the conversion
                character must be in lower-case.  

                To  use  floating  point  conversion,  the  program must
                reference the $$fpu global as follows:  

                        extern  int     $$fpu;

                If  this  is  not  done,  attempting to convert floating
                point will result in your program crashing.  

        Bugs 

                Only single precision conversion is done so far.  

                The  machine  must  support  FPU  floating  point, which

[[        C Compiler and Library]]                                     Page 5-10
        $$dtoa  Convert floating to ASCII


                implies EIS.  No compile-time test for C$$EIS is done.  

                Note:  This routine uses the table in the DOUTAB module 


[[        C Compiler and Library]]                                     Page 5-11
        $$fadd  Floating-point support, add/subtract


        5.8  Floating-point support, add/subtract              ______________ ________ ____________



                                   **********
                                   * $$fadd *
                                   **********



        File name:      fadd.mac


        Usage

                double
                $$fadd(a, b)            /* Floating add a + b   */

                double
                $$fsub(a, b)            /* Floating sub a - b   */

                double          a;
                double          b;

        Description

                Called by the compiler to compile floating-point.  

        Bugs 

                BEWARE:  Untested 


[[        C Compiler and Library]]                                     Page 5-12
        $$falo  Allocate memory for i/o subroutines


        5.9  Allocate memory for i/o subroutines              ________ ______ ___ ___ ___________



                                   **********
                                   * $$falo *
                                   **********



        File name:      iofalo.mac


        Usage

                mov     size,r0 ;Memory needed
                call    $$falo  ;Allocate it
                                ;return, r0 -> allocation
                                ;no room: return to caller via $$fope

        Description

                A  block  of  memory  is  allocated.  If this fails, the
                return is to the caller of fopen (or  fwild/fnext)  with
                i/o control blocks deleted as necessary.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-13
        $$fcsi  Scan file name for fopen


        5.10  Scan file name for fopen               ____ ____ ____ ___ _____



                                   **********
                                   * $$fcsi *
                                   **********



        File name:      iocsi.mac


        Usage

                mov     iov,r4  ;r4 -> iov
                call    $$fcsi  ;C$PMTR+0(r5) => file name
                                ;file name is parsed and fdb setup.
                                ;r0-r3 random
                                ;error: return to caller via $$fope

        Description

                Parse the file name argument, initializing the file data
                block.  Used on RSX only.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-14
        $$flsh  Flush output buffers


        5.11  Flush output buffers               _____ ______ _______



                                   **********
                                   * $$flsh *
                                   **********



        File name:      ioflsh.mac


        Usage
                mov     #iov,r4         ;r4 -> i/o vector
                call    $$flsh          ;Internal flush routine

                Return, all registers preserved.

        Description

                $$flsh is called by other file I/O routines to flush the
                current record buffer.  If this is the first call to  an
                output  routine for this file, $$flsh will be called and
                will allocate a buffer.  

                On  RSX,  if the file is open to the "command terminal",
                the flush is to stderr.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-15
        $$flun  Allocate a logical unit for fopen


        5.12  Allocate a logical unit for fopen               ________ _ _______ ____ ___ _____



                                   **********
                                   * $$flun *
                                   **********



        File name:      ioflun.mac


        Usage

                mov     iov,r4  ;r4 -> iov if any, else r4 := 0
                call    $$flun  ;Get a Lun slot, initialize fdb
                                ;return, r4 -> iov, r3 := lun
                                ;r0, r1 random
                                ;error: return to caller via $$fope
                                ;Note: available RSX luns start at 2,
                                ;while RT11 luns start at zero.

        Description

                Perform all initialization needed to allocate a new file
                descriptor.  

        Bugs 

                In  RSX  modes,  the maximum number of files that may be
                simultaneously open is defined at  assembly  time  by  a
                macro  (FSRSZ$)  which  is  expanded  when  fopen.mac is
                assembled.  The default FSRSZ$ parameter is 4.  This may
                be  modified by using the task builder /ACTFIL=n option.
                The default FSRSZ$ value may be specified when  the  RSX
                library is built by editing assembly parameter N$$FIL in
                RSX.MAC.  


[[        C Compiler and Library]]                                     Page 5-16
        $$fmul  Floating-point multiply/divide


        5.13  Floating-point multiply/divide               ______________ _______________



                                   **********
                                   * $$fmul *
                                   **********



        File name:      fmul.mac


        Usage

                double
                $$fmul(a, b);           /* Floating multiply    */
                double          a;
                double          b;

        Description

                Called   by   the  compiler  to  execute  floating-point
                multiply.  

        Bugs 

                BEWARE:  untested 


[[        C Compiler and Library]]                                     Page 5-17
        $$fopa  Open file (RT11 only)


        5.14  Open file (RT11 only)               ____ ____ _____ _____



                                   **********
                                   * $$fopa *
                                   **********



        File name:      iofopa.mac


        Usage

                mov     iov,r4  ;r4 -> iov
                mov     lun,r3  ;r3 := lun
                jmp     $$fopa  ;RT11 file open (ascii file spec.)
                                ;C$PMTR+0(r5) => ASCII file spec.
                                ;(may include file size for writes)
                                ;Parse the file using .CSISPC, open it,
                                ;returning to the caller via cret$ or
                                ;$$fope if error.

                mov     iov,r4  ;r4 -> iov
                mov     lun,r3  ;r3 := lun
                mov     dblk,r1 ;r1 -> Rad50 device descriptor, followed
                                ;by filesize word if write reqeust.
                jmp     $$fopr  ;open by Rad50 device descriptor
                                ;RT11 only -- used to open the device
                                ;for directory processing.  Exit via
                                ;cret$$ or $$fope if error.
                                ;If successful, the number of blocks in
                                ;the file is stored in the first word of
                                ;the block buffer.

        Description

                Actually   open   the   RT11  file,  doing  data  buffer
                management and post-open cleanup.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-18
        $$fopt  Scan options parameter for fopen


        5.15  Scan options parameter for fopen               ____ _______ _________ ___ _____



                                   **********
                                   * $$fopt *
                                   **********



        File name:      iofopt.mac


        Usage

                mov     iov,r4  ;r4 -> iov
                call    $$fopt  ;C$PMTR+2(r5) => options string
                                ;return: option flags in fdb
                                ;r0 random
                                ;error: return to caller via $$fope

        Description

                $$fopt  parses  the  options argument in calls to fopen,
                freopen(), or fwild().  It returns to  the  caller  (via
                $$fope) if the argument was incorrect.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-19
        $$fpar  Parse and Setup RMS Control Blocks


        5.16  Parse and Setup RMS Control Blocks               _____ ___ _____ ___ _______ ______



                                   **********
                                   * $$fpar *
                                   **********



        File name:      fpar.mac


        Usage

                mov     iov,r4  ;r4 -> iov
                call    $$fpar  ;C$PMTR+0(r5) => file name
                                ;file name is parsed and FAB/RAB etc.
                setup.
                                ;r0-r3 random
                                ;error: return to caller via $$fope

        Description

                Parse the file name argument, and dynamically create the
                RMS-11 specific blox (FAB, RAB, NAM block, DAT  block  &
                PRO block).  Used on RSX/RMS-11 only.  If possible, this
                routine establishes RMS-11 wildcard context.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-20
        $$fsav  Floating-point support routines


        5.17  Floating-point support routines               ______________ _______ ________



                                   **********
                                   * $$fsav *
                                   **********



        File name:      fis.mac


        Usage

                $$fsav                  /* Floating save        */
                $$frta                  /* Return to caller a   */
                $$frtb                  /* Return to caller b   */

        Description

                These routines are used internally by the floating-point
                simulation package.  They are  never  called  by  the  C
                program.  

        Bugs 

                BEWARE:  untested.  

                Note  also  that  these  routines  are single-precision,
                whereas   C   requires   double   precision.     When/if
                floating-point  becomes a reality, something better will
                have to be done.  


[[        C Compiler and Library]]                                     Page 5-21
        $$gcmd  Parse command line


        5.18  Parse command line               _____ _______ ____



                                   **********
                                   * $$gcmd *
                                   **********



        File name:      getcmd.mac


        Usage

                argc = $$gcmd(text, in, out, avp, task)
                char            *text;  /* Command line */
                char            **in;   /* stdin filename       */
                char            **out;  /* For stdout filename  */
                char            ***avp; /* Gets argv[] location */
                char            *task;  /* Task name if nonnull */

        Description:

                Parse  the  command line, building the argv[] table.  If
                I/O redirection is encountered, in and out are  modified
                accordingly.  

                NOTE:   $$gcmd  will  modify  text.  argv[] entries will
                point to bytes in text.  If not NULL, the task name will
                become  argv[0].   Unquoted  arguments will be forced to
                lowercase, duplicating the action of Vax-11 C.  

                $$gcmd() returns the number of arguments encountered.  

                $$gcmd() is called in the following fashion:  

                        /*
                         * Default input is on tty
                         */
                        char    **infile = &def_in;
                        char    *def_in = "tt:";
                        /*
                         * Default output is on tty
                         */
                        char    **outfile = &def_out;
                        char    *def_out = "tt:";
                        /*
                         * Define argv[] pointer and dummy command
                         * line.
                         */
                        char    **argvp;
                        char    *dummy = "main";
                        int     argc;

[[        C Compiler and Library]]                                     Page 5-22
        $$gcmd  Parse command line



                        ...

                        argc = $$gcmd((strlen(cmdlin) == 0) ?
                                                dummy : cmdlin,
                                &infile, &outfile, &argvp, $$task);

                        if (argc < 0)
                                error("Bad command line");
                        stdin = fopen(infile, "r");
                        if (**outfile == ">")
                                stdout = fopen(*outfile + 1, "a");
                        else    stdout = fopen(*outfile, "w");

        Bugs

                In  order  to compensate for a problem with native RT11,
                the "parity" bit is erased from the argument text.  This
                will  need  modification  to  handle the Dec Internation
                character set.  


[[        C Compiler and Library]]                                     Page 5-23
        $$get   Get a record


        5.19  Get a record               ___ _ ______



                                    *********
                                    * $$get *
                                    *********



        File name:      ioget.mac


        Usage

           RSX:
                mov     #iov,r4         ;r4 -> i/o vector
                mov     #buffer,r0      ;r0 -> buffer
                mov     buflen,r1       ;r1 := max. buffer size
                call    $$get           ;Get a record

                VF$EOF and/or VF$ERR are set on error or end of file.
                r0 := actual record length, -1 on error or end of file.

                Other registers preserved.

            RT11:
                mov     #blknbr,r0      ;r0 := block to read
                call    $$get           ;Get a block

                VF$EOF and/or VF$ERR are set on error or end of file.
                r0 is zero if success, -1 on error or end of file.

                Other registers preserved.

                clr     r0              ;End of file error
                jmp     $$geof          ;(called by $$getc)

        Description

                $$get is the internal "get a record" routine.  Note that
                the maximum record size (r1) is only needed on RSX.   It
                is fixed at 512.  bytes on RT11.  

                If the file is defined as "stream" (the "n" flag was not
                set when the file was opened using fopen()), the end  of
                the  line  will  be  represented  by  the  newline  (\n)
                character, and NULL's will be removed.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-24
        $$getc  Get characters


        5.20  Get characters               ___ __________



                                   **********
                                   * $$getc *
                                   **********



        File name:      iogetc.mac


        Usage

                mov     #iov,r4         ;r4 -> i/o vector
                call    $$getc          ;Get a character

        Description

                $$getc  is  the internal "get a byte" routine.  The next
                byte in the indicated file is returned in r0.  All other
                registers  are preserved.  $$getc will allocate a buffer
                if necessary.  

                This  routine  removes  all  NULL  bytes  and  <CR> from
                <CR><LF> sequences unless the file was opened  with  the
                'n' (nostream) option.  

        Bugs 

                RT11 uses .gtline to read from the user's terminal (thus
                tracking indirect command  files).   To  read  from  the
                physical terminal, fopen "TT:" using "n" mode.  

                RSTS/RT11  has  problems  reading using either .ttyin or
                .gtline.  There is  thus  special  case  code  to  force
                "native" system calls.  


[[        C Compiler and Library]]                                     Page 5-25
        $$gsa   Get-space routine


        5.21  Get-space routine               _________ _______



                                    *********
                                    * $$gsa *
                                    *********



        File name:      mygsa.mac


        Usage

          Internal

                Inputs:
                        r0 --> pool free-space list (not used)
                        r1 =   size (bytes) of requested/released block
                        r2 =   0 if allocating a block, address of first
                               word being released if deallocating.

                Outputs:
                        Successful allocation:
                                C-bit cleared and R0 --> allocated block
                        Unsuccessful allocation:
                                C-bit set
                        Deallocation:
                                Nothing returned

        Description

                RMS-11  pool  management  routine.  Used to allocate and
                deallocate space to meet the needs of RMS-11 operations. 

[[        C Compiler and Library]]                                     Page 5-26
        $$init  One-time initialization code


        5.22  One-time initialization code               ________ ______________ ____



                                   **********
                                   * $$init *
                                   **********



        File name:      init.mac


        Usage

          Internal

                $$init()

        Description

                When a C program is started, a command line is parsed to
                form the argv[] array and the  standard  input,  output,
                and error files are opened.  Note the following:  

                On  RSX11/M  (even emulated), argv[0] will be set to the
                task name.  On RT11 modes, argv[0]  will  be  set  to  a
                dummy value.  

                If  no  command  line  is passed to the program, it will
                prompt the task name (or "Argv") and read  a  line  from
                the command terminal.  To disable this, the user program
                may define a global flag as follows:  

                        $$narg = 1;
                        main (argv, argc) {
                        ...

                If $$narg is initialized non-zero and no command line is
                passed to the program, or if the initialization sequence
                fails  to  read  an argument, main() will be called with
                one argument.  

                The  command  line  prompt  may be changed from the task
                name (or "Argv") by defining a global string as follows: 

                        char *$$prmt = "Command line prompt"
                        main(argv, argc) {
                        ...

                On  Vax  VMS, the program may be installed as a "foreign
                command" by a command such as:  

                        $ command :== $disk:[dir]filename

[[        C Compiler and Library]]                                     Page 5-27
        $$init  One-time initialization code



                and executed by typing:  

                        $ command arg1 arg2

        Internal

                            MAINTAINERS, Please Note

                This   module   contains   code  that  is  sensitive  to
                particular releases of the  various  operating  systems.
                Also,  there  is  code  that is sensitive to the various
                types of operating  system  emulators.   The  maintainer
                should strive to keep all such code in this module.  

                This module has been tested on VMS V3.0 and V3.1, RSTS/E
                V7.1, RT11 V4.0, and RSX-11M  V4.0.   It  may  not  work
                correctly on earlier (or later) releases.  

                Note  especially  the "secret patch" to allow Decus C to
                read stream files  on  VMS  V3.0  (and  V3.1),  and  the
                command line parser for VMS version 3.0 and later.  This
                code will require examination on every release of VMS.  

        Diagnostics 

                Can't parse command line 

                ?C-Standard input, [filename]:  error text 

                ?C-Standard output, [filename]:  error text 

                ?C-No memory.  

                The  "can't  parse" message is given if the command line
                format is incorrect  (because  of  unbalanced  quotation
                marks, for example).  

                The "standard input" or "standard output" messages are a
                user error if input or output  are  redirected  and  the
                associated  files  cannot be opened.  The text should be
                self-explanatory.  

                The  "no  memory"  message  suggests  a  severe  case of
                program immensity.  

                All errors are fatal.  

        Bugs 

                On  RSTS/RSX,  command  lines  are  limited to 80 bytes,
                although 128 byte commands are feasable.   On  VMS  V3.0
                and V3.1, the command name includes the expanded form of
                the command name.  This means  that  long  command  name

[[        C Compiler and Library]]                                     Page 5-28
        $$init  One-time initialization code


                translations  coupled  with  long  argument  strings may
                cause the total argument  string  to  exceed  80  bytes.
                Such arguments will be truncated by the operating system
                without warning.  The work-around  is  to  make  use  of
                logical names:  

                        $ assign $disk[directory.subdirectory] bin
                        $ program :== $bin:prog

                The  expanded  form  of  the  "program"  command is just
                "bin:prog".  

                On  VMS  V3.0 and V3.1, the distributed RSX file service
                (FCS) refuses to open "stream Ascii" files.  This module
                contains  a  dynamically-installed  patch  to  the  open
                routine.  An error message will be printed if the  patch
                cannot  be installed correctly.  The VMS3.0 compile-time
                switch enables  this  patch.   There  is  also  code  in
                fopen.mac that is affected by this patch.  

                It  might be reasonable to make error messages non-fatal
                so $$init could be called by a user program.  

                On   RSX,   the  program  aborts  (by  executing  a  BPT
                instruction) if the program  fails  to  open  stderr  or
                obtain partition parameters.  


[[        C Compiler and Library]]                                     Page 5-29
        $$link  Print memory list


        5.23  Print memory list               _____ ______ ____



                                   **********
                                   * $$link *
                                   **********



        File name:      malink.mac


        Usage

                $$link();               /* Print memory list    */

                Return: all registers preserved


        Description

                Subroutine  $$link()  writes  the  allocation  list onto
                stderr.  It was written to debug  malloc()  but  may  be
                useful  for  debugging  programs  that write randomly in
                memory.  

                Note that it preserves all registers.  

        Diagnostics 

        Bugs 


[[        C Compiler and Library]]                                     Page 5-30
        $$ltoa  Convert long to Ascii


        5.24  Convert long to Ascii               _______ ____ __ _____



                                   **********
                                   * $$ltoa *
                                   **********



        File name:      ltoa.mac


        Usage

                $$ltoa(buff, radix, value);
                char            *buff;  /* Where it goes        */
                int             radix;  /* Conversion radix     */
                long            value;  /* What to convert      */

        Description

                Called  by  printf to convert a long integer from binary
                to Ascii, storing  the  result  in  buffer.   The  radix
                argument determines the conversion:  

                        d       Signed decimal
                        o       Octal
                        u       Unsigned decimal
                        X       Hex (10-15 = A-F)
                        x       Hex (10-15 = a-f)

        Bugs


[[        C Compiler and Library]]                                     Page 5-31
        $$main  Start of C programs


        5.25  Start of C programs               _____ __ _ ________



                                   **********
                                   * $$main *
                                   **********



        File name:      suport.mac


        Usage

                $$main::                /* Start of C programs  */

                extern int   $$opsy;    /* Operating system     */
                extern int   $$rsts;    /* Non-zero if RSTS/E   */
                extern int   $$vms;     /* Non-zero if VMS      */
                extern int   $$pos;     /* Non-zero if P/OS     */
                extern int   $$uic;     /* RSX: Default uic     */
                extern int   $$stnd;    /* Stack end point      */
                extern int   $$scca;    /* RT11: .scca control  */
                extern char  $$task[];  /* RSX: task name       */
                extern int   $$tick;    /* Clock interrupt rate */

          Internal

                extern int   (*$$pptr)();  /* Profile printer   */
                extern int   $$argc;    /* Argument count       */
                extern int   *$$argv[]; /* Argument list ptr.   */
                extern char  *$$mtop;   /* Free memory start    */
                extern char  *$$mend;   /* Free memory end      */

        Description

                This   module  contains  the  run-time  startoff  for  C
                programs.  It intializes the C environment and calls the
                main()  subroutine.   On  return  from the main program,
                exit() is called to close all files and  return  to  the
                operating system.  

                The following globals are defined in this module:  

                        $$opsy  Operating  system  unique  value.   This
                                value  is  7 on RT11, and set as per the
                                GTSK$ directive on RSX-based systems:
                                        RSX11-D         0.
                                        RSX11-M         1.
                                        RSX11-S         2.
                                        IAS             3.
                                        RSTS/E V7       4.
                                        VMS             5.

[[        C Compiler and Library]]                                     Page 5-32
        $$main  Start of C programs


                                        RSX11-M+        6.
                                        RT11            7.
                                        P/OS            9.

                        $$rsts  This value is non-zero if the program is
                                running  on  RSTS/E.   It is zero if the
                                program  is  running  native  RSX, RT11,
                                P/OS or VMS compatibility mode.

                        $$vms   This value is non-zero if the program is
                                running  (in  compatibility mode) on Vax
                                VMS.  It  is  zero  if  the  program  is
                                running  native  RSX,  RT11,  P/OS or on
                                RSTS/E.

                        $$pos   This value is non-zero if the program is
                                running on the Professional P/OS.  It is
                                zero if the program  is  running  native
                                RSX, RT11, or on RSTS/E or VMS.

                        $$stnd  The (top) end of the stack on entrance.

                        $$scca  On RT11, the .scca control  word.   This
                                is  needed  to  allow RSTS/E programs to
                                trap end of file.

                        $$task  On RSX, the task name in Ascii.

                        $$tick  The clock interrupt rate.  This  is  set
                                at  initialization  on  RT11  and on the
                                first call to time() or ftime() on RSX.

                        $$uic   On RSX, the default UIC word from GTSK$.

        Internal

                All  $$  values  are  for  internal  communication among
                runtime library routines.  I.e., let them alone.  

        Diagnostics 

                On RSX, the task aborts with a BPT if the standard error
                file  did  not  open.   Otherwise,   explanatory   error
                messages are printed.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-33
        $$mchk  Verify memory allocation pointers


        5.26  Verify memory allocation pointers               ______ ______ __________ ________



                                   **********
                                   * $$mchk *
                                   **********



        File name:      mamchk.mac


        Usage

                $$mchk();               /* Check memory list    */

        Description


                Subroutine  $$mchk()  checks  allocation  list pointers.
                The program is crashed by  calling  error  if  something
                goes wrong.  $$mchk preserves all registers.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-34
        $$narg  Define default for $$narg


        5.27  Define default for $$narg               ______ _______ ___ ______



                                   **********
                                   * $$narg *
                                   **********



        File name:      narg.mac


        Usage

                int     $$narg  = <value>;
                ...
                main() {
                        ...
                }

        Description

                If  no command line is provided when the program starts,
                the program will print a prompt on the command terminal,
                read  one  line and build the argv[] vector.  If this is
                undesirable, include a global definition  of  $$narg  in
                your C program as follows:  

                        int     $$narg  =       1;

                This  will  supress the command terminal read operation.
                The argv[] vector will be set to a dummy value.  

                If  the  user program does not define $$narg, it will be
                defined so as to enable the prompt.  

                Note that $$narg must be initilized at compilation time.
                It is tested  by  the  initialization  code  before  the
                main() program is called.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-35
        $$prmt  Null prompt pointer


        5.28  Null prompt pointer               ____ ______ _______



                                   **********
                                   * $$prmt *
                                   **********



        File name:      prmt.mac


        Usage
                char *$$prmt = "Prompt string";

        Description

                This  pointer  is  checked in $$init and if the user has
                defined $$prmt then it will be used as the  task  prompt
                instead  of  using  the  task  name on RSX or "Argv:" on
                RT-11.  

[[        C Compiler and Library]]                                     Page 5-36
        $$prnt  Print formatter


        5.29  Print formatter               _____ _________



                                   **********
                                   * $$prnt *
                                   **********



        File name:      doprnt.mac


        Usage

                $$prnt(format, argvec, iov)
                char            *format;
                int             *argvec[];
                FILE            *iov;

        Description

                $$prnt()   performs   all   formatting   operations  for
                printf(),  sprintf(),  and  fprintf().   The  formatting
                options are described int the documentation of printf(). 

        Bugs 

                $$prnt()  is  functionally  identical  to  the _doprnt()
                module in Unix and Vax-11 C  libraries.   Unfortunately,
                the '_' conflicts with RSX FCS library conventions.  


[[        C Compiler and Library]]                                     Page 5-37
        $$put   Write a record -- RSX only


        5.30  Write a record -- RSX only               _____ _ ______ __ ___ ____



                                    *********
                                    * $$put *
                                    *********



        File name:      ioput.mac


        Usage

                mov     #bufadr,r0      ;r0 -> buffer start
                mov     nbytes,r1       ;r1 := number of bytes
                mov     #iov,r4         ;r4 -> i/o vector
                call    $$put           ;Internal put buffer routine

                Return, r1..r4 preserved.

        Description

                $$put  is called by RSX-mode routines to write a record.
                $$put only runs under the  RSX  library.   Using  it  in
                RT11-mode  will  cause the job to abort with a BPT trap.
                The byte count may be zero for RSX Terminal I/O.  

                If  output  is  to  a  terminal,  stderr will be flushed
                (first).  

                If  the  RMS-11(V2)  version  is  in use, $$put supports
                updating of records within an existing sequential  file,
                if the new record is the same length as the old one.  
        Bugs 


[[        C Compiler and Library]]                                     Page 5-38
        $$putc  Output one character to a file


        5.31  Output one character to a file               ______ ___ _________ __ _ ____



                                   **********
                                   * $$putc *
                                   **********



        File name:      ioputc.mac


        Usage

                mov     #iov,r4         ; r4 -> I/O vector
                mov     byte,r0         ; r0 := byte to output
                call    $$putc

        Description

                $$putc is the internal call to write one character to an
                indicated file.  On return, all registers are preserved,
                even  r0.   $$putc  will  allocate  a  record  buffer if
                necessary.  If an error is detected, $$putc will  return
                to the original (C-language) caller.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-39
        $$qiow  Call RSX executive service


        5.32  Call RSX executive service               ____ ___ _________ _______



                                   **********
                                   * $$qiow *
                                   **********



        File name:      ioqiow.mac


        Usage

                mov     <I/O function code>,r0
                mov     IOV pointer,r4
                mov     <iopl parameters> onto the stack, right to left
                call    $$qiow
                bcs     <error>

        Description

                Issue  a  qio$  directive  for  all I/O requests needing
                such.  Uses r0, r1.  

                This  routine is used only in the RSX library.  Using it
                in the RT11 library will cause the program to abort with
                by executing a BPT instruction.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-40
        $$rtim  Date and time conversion


        5.33  Date and time conversion               ____ ___ ____ __________



                                   **********
                                   * $$rtim *
                                   **********



        File name:      rtime.mac


        Usage

                $$rtim(buffer);
                struct TIME {
                        int     year;   /* G.TIYR  year - 1900  */
                        int     month;  /* G.TIMO  Jan. = 1     */
                        int     day;    /* G.TIDA               */
                        int     hour;   /* G.TIHR  00 .. 23     */
                        int     minute; /* G.TIMI  00 .. 59     */
                        int     second; /* G.TISC  00 .. 59     */
                        int     tick;   /* G.TICT  00 .. tsec-1 */
                        int     tsec;   /* G.TICP  tick/second  */
                } buffer;

        Description

                Stores  the  current  time  of  day  in the buffer.  The
                format is compatible with the  RSX11-M  GTIM$  executive
                service.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-41
        $$scan  Formatted input conversion


        5.34  Formatted input conversion               _________ _____ __________



                                   **********
                                   * $$scan *
                                   **********



        File name:      doscan.mac


        Usage

                $$scan(fmt, args, iov)
                char            *fmt;   /* Format string        */
                int             *arg[]; /* Arg vector           */
                FILE            *iov;   /* File descriptor      */

        Description

                $$scan()   does  parsing  for  scanf(),  etc.   See  the
                description of scanf() for more details.  

        Bugs 

                $$scan()  is  functionally  identical  to  the _doscan()
                routine in Unix and Vax-11 C libraries.   Unfortunately,
                the  leading  '_'  conflicts  with  RSX FCS library name
                conventions.  


[[        C Compiler and Library]]                                     Page 5-42
        $$svr1  Save registers r1-r5 on the stack


        5.35  Save registers r1-r5 on the stack               ____ _________ _____ __ ___ _____



                                   **********
                                   * $$svr1 *
                                   **********



        File name:      savr1.mac


        Usage

                jsr     r5,$$svr1       ;Save r1-r5 on the stack
                ...
                return                  ;Restore r1-r5 and return to
                caller

        Description

                Save  general registers r1-r5 on the stack and return to
                the caller.  When the caller  executes  an  return  (rts
                pc), it will cause the original r1-r5 to be restored and
                the program will return to the original caller.  

                On return, the caller's registers are as follows:  

                        R1      02(SP)
                        R2      04(SP)
                        R3      06(SP)
                        R4      10(SP)
                        R5      12(SP)
                        PC      14(SP)  Return to original user

        Bugs

                Except for the C-bit, condition codes are not preserved. 


[[        C Compiler and Library]]                                     Page 5-43
        $$tens  Conversion table for dtoa, atof


        5.36  Conversion table for dtoa, atof               __________ _____ ___ _____ ____



                                   **********
                                   * $$tens *
                                   **********



        File name:      doutab.mac


        Usage

                extern double $$tens[];


        Description

                $$tens[i] has 10^i for the range 0..35 

[[        C Compiler and Library]]                                     Page 5-44
        $$utim  Convert $$rtim buffer to Unix time


        5.37  Convert $$rtim buffer to Unix time               _______ ______ ______ __ ____ ____



                                   **********
                                   * $$utim *
                                   **********



        File name:      utime.mac


        Usage

                long
                $$utim(buffer);
                struct TIME {
                        int     year;   /* G.TIYR  year - 1900  */
                        int     month;  /* G.TIMO  Jan. = 1     */
                        int     day;    /* G.TIDA               */
                        int     hour;   /* G.TIHR  00 .. 23     */
                        int     minute; /* G.TIMI  00 .. 59     */
                        int     second; /* G.TISC  00 .. 59     */
                        int     tick;   /* G.TICT  00 .. tsec-1 */
                        int     tsec;   /* G.TICP  tick/second  */
                } buffer;

        Description

                The  user  calls $$rtim() to initialize a buffer.  Then,
                $$utim will convert buffer contents  to  the  number  of
                seconds since Jan 1, 1970.  

                Note:   $$utim()  does not compensate for local timezone
                or daylight savings time.  

        Bugs 

                This routine works only in the range:  

                        1970 <= year < 2100


[[        C Compiler and Library]]                                     Page 5-45
        abort   Abort program with a BPT trap


        5.38  Abort program with a BPT trap               _____ _______ ____ _ ___ ____



                                    *********
                                    * abort *
                                    *********



        File name:      abort.mac


        Usage

                abort()

        Description

                After  closing all files, the program exits by executing
                a BPT trap.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-46
        abs     Integer absolute value


        5.39  Integer absolute value               _______ ________ _____



                                     *******
                                     * abs *
                                     *******



        File name:      abs.mac


        Usage

                abs(val)
                int             val;

        Description

                Return absolute value of the integer argument.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-47
        alloc   Allocate memory


        5.40  Allocate memory               ________ ______



                                    *********
                                    * alloc *
                                    *********



        File name:      alloc.mac


        Usage

                char *
                alloc(n);               /*   -1 if no space     */

        Description

                Allocate  the  requested  number  of  bytes, returning a
                pointer  to  the  first.   The  program  image  will  be
                expanded as needed.  

                alloc()  returns  -1 if the requested space could not be
                allocated.  

                free() is used to return the buffer to free space.  

                See  also  the  description  of  malloc(), realloc() and
                sbrk().  

        Diagnostics 

        Bugs 

                alloc() is obsolete.  Use malloc() for new programs.  

[[        C Compiler and Library]]                                     Page 5-48
        ascr50  Ascii to Radix-50 conversion


        5.41  Ascii to Radix-50 conversion               _____ __ ________ __________



                                   **********
                                   * ascr50 *
                                   **********



        File name:      ascr50.mac


        Usage

                ascr50(count, input, output)
                int             count;
                int             *output;
                char            *input;

        Description

                Convert  'count'  characters from ascii to Radix 50.  If
                there aren't a multiple  of  3  characters,  blanks  are
                padded  on  the  end.   The ascii string is moved to the
                output when finished.  The input and output areas may be
                the same since three input characters are read for every
                two bytes of output.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-49
        asl$l   Shift long << long


        5.42  Shift long << long               _____ ____ __ ____



                                    *********
                                    * asl$l *
                                    *********



        File name:      asll.mac


        Usage

                long
                asl$l(l, n)
                long            l;
                long            n;

                long
                asr$l(l, n)
                long            l;
                long            n;

        Description

                Performs  shifting  of long by long.  Only the low-order
                six bits of the shift argument are  examined.   This  is
                compatible with the hardware ASH instruction.  

                Note that, if n is negative:  

                        (l << n) == (l >> (-n))

        Bugs


[[        C Compiler and Library]]                                     Page 5-50
        asl$li  Shift long << integer


        5.43  Shift long << integer               _____ ____ __ _______



                                   **********
                                   * asl$li *
                                   **********



        File name:      aslli.mac


        Usage

                long
                asl$li(l, n)
                long            l;
                int             n;

                long
                asr$li(l, n)
                long            l;
                int             n;

        Description

                Performs   arithmetic   shifting   for   integer   shift
                arguments.  Note that only the low-order six bits of the
                shift  argument  are  examined.  This is compatible with
                the hardware shift instruction.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-51
        asr$u   Right shift unsigned >> integer


        5.44  Right shift unsigned >> integer               _____ _____ ________ __ _______



                                    *********
                                    * asr$u *
                                    *********



        File name:      asru.mac


        Usage

                unsigned
                asr$u(u, n)
                unsigned        u;
                int             n;

        Description

                Performs  u  >>  n  for  unsigneds.   Note that, if n is
                negative, it acts as if (u << (-n)) were executed.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-52
        atod    Convert Ascii to double floating


        5.45  Convert Ascii to double floating               _______ _____ __ ______ ________



                                    ********
                                    * atod *
                                    ********



        File name:      atod.mac


        Usage

                double
                atod(buffer)
                char            *buffer;

        Description

                Converts   a   double-precision  floating  point  number
                written in scientific notation from ASCII to a  "double"
                number.   The  BNF for numbers which can decoded by this
                routine follows:  

                    <number> := <sign> <real number>
                    <real number> :=
                        <decimal number>
                        | <decimal number> <exponent>
                        | <exponent>
                    <decimal number> :=
                        <integer>
                        | <integer> .
                        | . <integer>
                        | <integer> . <integer>
                    <integer> := <digit> | <integer> <digit>
                    <exponent> :=
                        { E | e | D | d } <sign> <integer>
                    <digit> := 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
                    <sign> := + | - | <empty>

                The  conversion  stops on the first non-legal character.
                (Note:  if this routine is declared type char *, it will
                return a pointer to the first non-legal character.) 

        Bugs 

        Internal 

                If   the  C  library  is  compiled  using  "inline  EIS"
                (C$$EIS=1), hardware floating point is also required.  

                Note:  This routine uses the table in the DOUTAB module. 

[[        C Compiler and Library]]                                     Page 5-53
        atod    Convert Ascii to double floating




[[        C Compiler and Library]]                                     Page 5-54
        atof    Convert Ascii to double floating


        5.46  Convert Ascii to double floating               _______ _____ __ ______ ________



                                    ********
                                    * atof *
                                    ********



        File name:      atof.mac


        Usage

                double
                atof(buffer)
                char            *buffer;

        Description

                Converts   a   double-precision  floating  point  number
                written in scientific notation from ASCII to a  "double"
                number.   The  BNF for numbers which can decoded by this
                routine follows:  

                    <number> := <sign> <real number>
                    <real number> :=
                        <decimal number>
                        | <decimal number> <exponent>
                        | <exponent>
                    <decimal number> :=
                        <integer>
                        | <integer> .
                        | . <integer>
                        | <integer> . <integer>
                    <integer> := <digit> | <integer> <digit>
                    <exponent> :=
                        { E | e | D | d } <sign> <integer>
                    <digit> := 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
                    <sign> := + | - | <empty>

                The  conversion  stops on the first non-legal character.
                (Note:  if this routine is declared type char *, it will
                return a pointer to the first non-legal character.) 

        Bugs 

        Internal 

                If   the  C  library  is  compiled  using  "inline  EIS"
                (C$$EIS=1), hardware floating point is also required.  

                Note:  This routine uses the table in the DOUTAB module. 

[[        C Compiler and Library]]                                     Page 5-55
        atof    Convert Ascii to double floating




[[        C Compiler and Library]]                                     Page 5-56
        atofd   Convert ASCII to floating -- dummy


        5.47  Convert ASCII to floating -- dummy               _______ _____ __ ________ __ _____



                                    *********
                                    * atofd *
                                    *********



        File name:      atofd.mac


        Usage

                double
                atof(buffer)
                char    *buffer;

        Description

                This  is  a  dummy routine that is always present in the
                Decus C run-time library.   If  a  program  attempts  to
                convert  an  ASCII  string to a floating point value (by
                calling  scanf()  with  a  '%f'  format  effector),  the
                program will crash.  

                If  floating  point conversion is needed, the conversion
                routine must be named in the link or task-build  command
                line as follows:  

                  RSX:  TKB file=file,c:atof,c:c/lb
                  RT11: LINK file,c:atof,c:suport,c:clib/bot:2000

        Bugs


[[        C Compiler and Library]]                                     Page 5-57
        atoi    Convert Ascii to integer


        5.48  Convert Ascii to integer               _______ _____ __ _______



                                    ********
                                    * atoi *
                                    ********



        File name:      atoi.mac


        Usage

                atoi(p)
                char            *p;

        Description

                Convert   string   to  integer.   No  data  checking  is
                performed.   The   conversion   stops   at   the   first
                non-integer.   Leading  spaces,  tabs, plus-signs and/or
                newlines are ignored.  The integer may be preceeded by a
                minus sign.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-58
        atoi8   Convert Ascii octal number to integer


        5.49  Convert Ascii octal number to integer               _______ _____ _____ ______ __ _______



                                    *********
                                    * atoi8 *
                                    *********



        File name:      atoi8.mac


        Usage

                atoi8(p)
                char    *p;

        Description

                Convert  an  Ascii  octal number to an integer.  No data
                checking is performed.   The  conversion  stops  at  the
                first   non-octal   integer.    Leading   spaces,  tabs,
                plus-signs and/or newlines are ignored.  


[[        C Compiler and Library]]                                     Page 5-59
        atol    Convert Ascii to long


        5.50  Convert Ascii to long               _______ _____ __ ____



                                    ********
                                    * atol *
                                    ********



        File name:      atol.mac


        Usage

                long
                atol(p)
                char            *p;

        Description

                Convert   string   to  integer.   No  data  checking  is
                performed.   The   conversion   stops   at   the   first
                non-integer.   Leading  spaces,  tabs, plus-signs and/or
                newlines are ignored.  The integer may be preceeded by a
                minus sign.  


        Bugs 


[[        C Compiler and Library]]                                     Page 5-60
        brk     Change memory allocation


        5.51  Change memory allocation               ______ ______ __________



                                     *******
                                     * brk *
                                     *******



        File name:      brk.mac


        Usage

                char *
                brk(addr);
                int             *addr;

        Description

                brk()  sets  the  run-time  library's  "top  of  memory"
                pointer to addr.  This value should have  been  returned
                by  a  previous  call  to  sbrk().  Intervening calls to
                malloc() or file open routines may cause  memory  to  be
                corrupted by calling brk().  

        Diagnostics 

                Returns  0 if the brk() argument is reasonable.  Returns
                -1 if it is greater than  the  current  top  of  memory.
                (Use sbrk() to increase memory allocation.) 

        Bugs 



[[        C Compiler and Library]]                                     Page 5-61
        call    Call (Fortran) subroutine from C


        5.52  Call (Fortran) subroutine from C               ____ _________ __________ ____ _



                                    ********
                                    * call *
                                    ********



        File name:      call.mac


        Usage

                return_value = call(routine, count, &arg1, ... &argN);
                extern int routine();   /* PDP-11 function name */
                int        count;       /* Number of arguments  */

        Description

                C Library user-callable interface between C programs and
                subroutines which  follow  the  standard  PDP11  calling
                sequence.  Note that call() saves and restores registers
                r2-r5.  

                The arguments are as follows:  

                        routine         The name of the PDP11 routine to
                                        be called.

                        count           The number of arguments  in  the
                                        calling sequence.

                        arg1            The first argument.

                For example:  

                        extern int      sort();
                        int             data_to_sort[NDATA];
                        int             ndata = NDATA;

                        call(sort, 2, &data_to_sort, &ndata);

                Note  that,  if  the  called function returns some other
                datatype such as a long, the routine and call() must  be
                correctly declared:  

                        long            call();
                        long            myfun();
                        long            larg;
                        long            result;

                        result = call(myfun, 1, &larg);

[[        C Compiler and Library]]                                     Page 5-62
        call    Call (Fortran) subroutine from C



                If  call()  is  being  used  to return several different
                datatypes, type coersion may be effective:  

                        int             call();
                        long            myfun();
                        long            larg;
                        long            result;

                        result = (long)call(myfun, 1, &larg);

        Bugs:

                WARNING:   watch  out  for trouble if the PDP-11 routine
                does any I/O.  Floating-point data return has  not  been
                implemented.  


[[        C Compiler and Library]]                                     Page 5-63
        callc   Call (Fortran) subroutine from C


        5.53  Call (Fortran) subroutine from C               ____ _________ __________ ____ _



                                    *********
                                    * callc *
                                    *********



        File name:      callc.mac


        Usage

                integer callc

                ivalue = callc(routine, arg1, ... argN)

        Description

                User-callable  interface  between  Fortran  programs and
                subroutines written in C.  

                The arguments are as follows:  

                        routine         The name of the C routine to  be
                                        called.

                        arg1            The   (location  of  the)  first
                                        argument.

                For example:  

                        call callc(sort, table, nelement)

        Bugs

                There  will  be I/O library conflicts since C files have
                not been initialized.  

                The  following  problem  will occur if a C subroutine is
                called from a Fortran main program:  

                The  C  subroutine  refers  to the save register routine
                (CSV$) which refers to the C main program.   This  pulls
                in a large amount of I/O dependent code, which may cause
                conflicts.  

                What is worse is that there will be two main programs.  

                It  is  therefore  recommended  that  there  be a C main
                program that calls  Fortran  subroutines  that  may,  in
                turn, call C subroutines.  

[[        C Compiler and Library]]                                     Page 5-64
        callc   Call (Fortran) subroutine from C



                The  programmer  can  also  define  a dummy program that
                resolves  the  globals  referenced  by  CSV$  or  modify
                callc.mac to provide the necessary globals.  


[[        C Compiler and Library]]                                     Page 5-65
        caller  Return name of profiled caller


        5.54  Return name of profiled caller               ______ ____ __ ________ ______



                                   **********
                                   * caller *
                                   **********



        File name:      caller.mac


        Usage

                char    *
                caller();

        Description

                If  the  routine  which  called the current function was
                compiled using the profile option,  caller()  returns  a
                pointer  to  the  name  of the calling function.  If the
                calling  function  was  not  compiled   with   profiling
                enabled, a pointer to the null string is returned.  

                Example:  

                        foo()
                        {
                                foobar();
                        }

                        foobar()
                        {
                                extern char *caller();

                                printf("foobar was called by %s\n",
                                                caller());
                        }


        Internal

                Warning  --  this  routine is sensitive to the format of
                the environment frame and  profile  information  layout.
                If  csv$,  pcsv$,  or $$prof change, this may have to be
                modified.  
        Bugs 


[[        C Compiler and Library]]                                     Page 5-66
        calloc  Allocate and Initialize Memory


        5.55  Allocate and Initialize Memory               ________ ___ __________ ______



                                   **********
                                   * calloc *
                                   **********



        File name:      calloc.mac


        Usage

                char *
                calloc(n, m);           /* NULL if no space     */
                int             n;      /* Number of elements   */
                int             m;      /* Size of an element   */

        Description

                Calloc()  allocates  space  for n elements, each m bytes
                long.  On return, the space  is  zero'ed.   The  program
                image will be expanded as needed.  

                If  the  requested  space  cannot be allocated, calloc()
                returns NULL.  

                See  also  the  description  of  malloc(), realloc() and
                sbrk().  

                The space is returned by calling free().  

        Diagnostics 

        Bugs 


[[        C Compiler and Library]]                                     Page 5-67
        calltr  Trace Path to the Caller


        5.56  Trace Path to the Caller               _____ ____ __ ___ ______



                                   **********
                                   * calltr *
                                   **********



        File name:      calltr.mac


        Usage

                calltrace(outfd);
                FILE            *outfd;

        Description

                calltrace() prints the calling path (from main()) to the
                routine that called calltrace()) on the indicated  file.
                The path is printed on one line as:  

                        [ main sub1 sub2 ]

                If  a  subroutine  within the path was not compiled with
                profiling, or does not  start  with  a  call  to  the  C
                register  register  save  routine, it will be printed as
                <nnnnnn> (where <nnnnnn> is the  octal  address  of  the
                entry  to the routine).  Note that the last entry on the
                line is the routine that invoked calltrace().  

                A  call  trace  will  be printed on exit if profiling is
                enabled and the program aborts or calls error().  

        Internal 

                Warning  --  this  routine is sensitive to the format of
                the environment frame and  profile  information  layout.
                If  csv$,  pcsv$,  or $$prof change, this may have to be
                modified.  

                A  special  entry  for error() is provided, which allows
                the proper "bug" address to be  displayed,  rather  than
                the return address of error() itself.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-68
        clearerr        Clear file error flags


        5.57  Clear file error flags               _____ ____ _____ _____



                                  ************
                                  * clearerr *
                                  ************



        File name:      cleare.mac


        Usage

                clearerr(iop);
                FILE            *iop;

        Description

                Clear  the  error  flags  for an open file.  This may be
                needed for interaction with the user's console terminal. 

        Bugs 


[[        C Compiler and Library]]                                     Page 5-69
        concat  Concatenate strings


        5.58  Concatenate strings               ___________ _______



                                   **********
                                   * concat *
                                   **********



        File name:      concat.mac


        Usage

                char *
                concat(out, in0, in1, ..., inN, 0);
                char            *out;
                char            *in0, in1, ... inN;

        Description

                Concat  concatenates the argument strings.  It returns a
                pointer to the first byte of out.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-70
        copy    Copy a given number of bytes


        5.59  Copy a given number of bytes               ____ _ _____ ______ __ _____



                                    ********
                                    * copy *
                                    ********



        File name:      copy.mac


        Usage

                char *
                copy(out, in, nbytes)
                char            *out;   /* Output vector        */
                char            *in;    /* Input vector         */
                unsigned int    count;  /* Bytes to copy        */

        Description

                Copy  the  indicated number of bytes from the input area
                to the output area.  Return a pointer to the first  free
                byte in the output area.  

                The copying will be faster if out and in are either both
                even or both odd addresses.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-71
        cpystr  String copy


        5.60  String copy               ______ ____



                                   **********
                                   * cpystr *
                                   **********



        File name:      cpystr.mac


        Usage

                char *
                cpystr(out, in);
                char            *out;
                char            *in;

        Description

                Copy "in" to "out".  Return a pointer to the end of out.
                This allows the following usage:  

                        char            *ptr;
                        char            buffer[BUFSIZ];
                        extern char     *cpystr();

                        ptr = cpystr(buffer, text);
                        ptr = cpystr(ptr, more_text);

                The above sequence appends more_text to the copy of text
                already moved into the buffer.  

        Bugs 



[[        C Compiler and Library]]                                     Page 5-72
        csv$    C register save and restore


        5.61  C register save and restore               _ ________ ____ ___ _______



                                    ********
                                    * csv$ *
                                    ********



        File name:      csv.mac


        Usage

                jsr     r5,csv$
                ...
                jmp     cret$

        Description

                        C program Run-time Environment

                Each  C  subroutine starts with a call to CSV$ and exits
                by jumping to CRET$.  Upon exit, the stack need  not  be
                equal to its value on entrance.  

                During  the  execution of all C subroutines, register R5
                points  to   the   current   "environment."   Within   a
                subroutine, it appears as follows:  

                         _______________
                        |               |
                  SP -> | 1st loc. var. | -10(R5)       C$AUTO-2(R5)
                        |_______________|
                        |               |
                        | Saved R2      |  -6(R5)
                        |_______________|
                        |               |
                        | Saved R3      |  -4(R5)
                        |_______________|
                        |               |
                        | Saved R4      |  -2(R5)
                        |_______________|
                        |               |
                  R5 -> | Saved R5      |
                        |_______________|
                        |               |
                        | Return add.   |  +2(R5)
                        |_______________|
                        |               |
                        | First arg.    |  +4(R5)       C$PMTR+0(R5)
                        |_______________|
                        |               |

[[        C Compiler and Library]]                                     Page 5-73
        csv$    C register save and restore


                        | Second arg.   |  +6(R5)       C$PMTR+2(R5)
                        |_______________|

                Within  a subroutine, Registers R0-R4 and the top of the
                stack, (sp) are available for use.  Registers R0 and  R1
                are not preserved by subroutines and may be used to pass
                a return value.  

                R5  must  not be modified by a subroutine.  All variable
                addressing must be done by offsets  to  R5.   Subroutine
                arguments  must  be  accessed  by  reference  to C$PMTR.
                Subroutine local variables must be accessed by reference
                to   C$AUTO.    This  permits  modification  of  calling
                sequences without rewriting all subroutines.  

                CSV$ refers to global symbol $$main to call the run-time
                startup program from the (RSX) library.  

        Internal 

                The   global  symbols  needed  for  the  Whitesmith's  C
                compiler are also included.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-74
        ctime   Convert time value to ascii


        5.62  Convert time value to ascii               _______ ____ _____ __ _____



                                    *********
                                    * ctime *
                                    *********



        File name:      ctime.mac


        Usage

                #include <time.h>

                char *
                ctime(tvecp)
                long            *tvec;  /* Time value pointer   */

                char *
                asctime(tm)
                struct tm       *tm;    /* Time buffer pointer  */

        Description

                ctime()  converts a time value, as returned by time() to
                an  ascii  string.   For  compatibility  with   previous
                versions, ctime(0) obtains and converts the current time
                of day.  Note, however, that ctime(0) is not portable.  

                asctime()   converts  a  time  vector,  as  returned  by
                localtime() to an ascii string.  

                The string is statically allocated.  It has the format 

                        Sun Sep 16 01:03:52 1973\n\0
                        012345678901234567890123 4 5
                        0         1         2

                All  the  fields  have  constant  width.   To remove the
                trailing newline, just:  

                        char            *tp;
                        extern char     *ctime();
                        int             tvec[2];

                        time(&tvec);            /* Get time     */
                        tp = ctime(&tvec);      /* in Ascii     */
                        tp[24] = '\0';          /* Fix newline  */

        Bugs


[[        C Compiler and Library]]                                     Page 5-75
        ctime   Convert time value to ascii


                There is no range checking on the information passed.  


[[        C Compiler and Library]]                                     Page 5-76
        ctype   Character classification type table


        5.63  Character classification type table               _________ ______________ ____ _____



                                    *********
                                    * ctype *
                                    *********



        File name:      ctype.mac


        Usage

                #include <ctype.h>

                        mov     #MASK,r0
                        jmp     $$ctype

        Description

                This  module contains the bit-mask table and common code
                for the is...  and to...  functions.  

        Bugs 

                No provisions are made for national letters.  

                Maintainers  note  that  source  for  a  test program is
                included.  

[[        C Compiler and Library]]                                     Page 5-77
        ddtoa   Convert floating to ASCII -- dummy


        5.64  Convert floating to ASCII -- dummy               _______ ________ __ _____ __ _____



                                    *********
                                    * ddtoa *
                                    *********



        File name:      dtoad.mac


        Usage

                $$dtoa(buff, value, field, dplace)
                char    *buff;          /* Where it goes        */
                double  value;          /* What to convert      */
                int     field;          /* Maximum field width  */
                int     dplace;         /* Decimal part width   */

        Description

                This  is  a  dummy routine that is always present in the
                Decus C run-time library.   If  a  program  attempts  to
                convert  a  floating  point  value  to ascii (by calling
                printf() with a '%f' format effector), an error  message
                will be generated.  

                If  floating  point conversion is needed, the conversion
                routine must be named in the link or task-build  command
                line as follows:  

                  RSX:  TKB file=file,c:dtoa,c:c/lb
                  RT11: LINK file,c:dtoa,c:suport,c:clib/bot:2000

        Bugs


[[        C Compiler and Library]]                                     Page 5-78
        delete  Delete a named file


        5.65  Delete a named file               ______ _ _____ ____



                                   **********
                                   * delete *
                                   **********



        File name:      delete.mac


        Usage

                delete(filename)
                char            *filename;

        Description


                Delete the named file.  Returns 1 on success, 0 on error
                (such as file not found).  If an  error  occurs,  $$ferr
                can be checked for the error code.  

                On RSX modes, the filename as passed need not include an
                explicit  version  number.    If   none   is   provided,
                file.nam;0  will  be  deleted.   Note  that the filename
                returned  by  fgetname()  always  includes  an  explicit
                version.  

                On  RT  modes, the only error ever returned is "File not
                found".  

        Bugs 

                On RSX/VMS, the file must be in the user's current ("SET
                DEFAULT") directory.  

                On RSTS, "SY0:" cannot be distinguished from "SY:".  


[[        C Compiler and Library]]                                     Page 5-79
        div$li  Long division and modulus


        5.66  Long division and modulus               ____ ________ ___ _______



                                   **********
                                   * div$li *
                                   **********



        File name:      divl.mac


        Usage

                div$li(long, integer)
                div$l(long, long)
                mod$li(long, integer)
                mod$l(long, long)

        Description

                Division  with long result.  Called by the compiler when
                the appropriate code sequences are encountered.  

        Bugs 

                Warning  --  an  internal  version  of cret$ is present.
                Change one, change both.  


[[        C Compiler and Library]]                                     Page 5-80
        eis$i   EIS emulator module


        5.67  EIS emulator module               ___ ________ ______



                                    *********
                                    * eis$i *
                                    *********



        File name:      eis.mac


        Usage

                asl$i(a, b);            /* Execute a << b       */
                asr$i(a, b);            /* Execute a >> b       */
                mul$i(a, b);            /* Execute a * b        */
                div$i(a, b);            /* Execute a / b        */
                mod$i(a, b);            /* Execute a % b        */

        Description

                All  arguments  are integers.  These routines are called
                by the C compiler to perform the indicated operations.  

                The  module  may  be conditionally compiled to generated
                hardware EIS operations.  Edit RT11.MAC  or  RSX.MAC  to
                define C$$EIS as needed:  

                        0       Emulate EIS operations
                        1       Generate EIS operations

                C$$EIS is defaulted zero for RT11, non-zero for RSX.  

                If n is negative, x << n == x >> (-n) and v.v.  

                Note:   div$i  returns the remainder in r1.  This may be
                useful for assembly-language programs that need both the
                quotient and remainder.  

                To   explicitly  position  this  module  in  an  overlay
                structure, refer to the title, EIS$I.  

        Bugs 

                Divide   by  zero  yields  zero  for  the  quotient  and
                remainder.  

[[        C Compiler and Library]]                                     Page 5-81
        envsave Multi-level function return


        5.68  Multi-level function return               ___________ ________ ______



                                   ***********
                                   * envsave *
                                   ***********



        File name:      envset.mac


        Usage

                int *
                envsave();

                envreset(frame, hval, lval)
                int             *frame; /* Frame pointer        */
                int             hval;   /* High-order return    */
                int             lval;   /* Low-order return     */

        Description

                These  functions  permit  a  multi-level return from a C
                function to one of its dynamic ancestors in the stack.  

                Envsave()  returns  the  address  of  the  frame  of its
                caller.  Later calls to envreset() with this pointer  as
                an  argument  will  create  the  illusion  that the last
                function invoked by the  caller  of  envsave()  returned
                directly  with  a  value  equal  to  the parameter(s) to
                envreset().  

                Envreset()  simulates  a  return  to  the function whose
                frame pointer matches frame (the result  of  a  previous
                call  to  envsave()).  Envreset() may be made to look as
                if it is returning a one or two word value.  If  only  a
                single   integer   value   is   passed  in  addition  to
                envreset(), it looks as if a 1-word value was  returned.
                If two integers (or equivalently, a long) are specified,
                it looks like a long is returned.  Thus any 1 or 2  word
                value  may  be returned because of the lax type checking
                in C.  

                It  is  catastrophic  to attempt to return to a function
                which has itself already returned!!!  

                The   following   illustrates   use   of  envsave()  and
                envreset():  

                        int     *save_frame;


[[        C Compiler and Library]]                                     Page 5-82
        envsave Multi-level function return


                        process() {
                          ...
                          save_frame = envsave();
                          if (subroutine()) {
                            /*
                             * Success
                             */
                          }
                          else {
                            /*
                             * Failure
                             */
                          }
                        }

                        subroutine() {
                          /*
                           * Abort on error
                           */
                          if (...)
                            envreset(save_frame, 0)
                          /*
                           * Success
                           */
                          return(1);
                        }

                When  subroutine() detects an error, it calls envreset()
                to  return  to  the  caller  of  process(),  passing   a
                "failure" flag.  

        Bugs 

                If   the  caller  of  envsave()  has  already  returned,
                disaster will result.  

                It    is    highly   recommended   that   programs   use
                setjmp/longjmp instead.  


[[        C Compiler and Library]]                                     Page 5-83
        error   Error exit from C programs


        5.69  Error exit from C programs               _____ ____ ____ _ ________



                                    *********
                                    * error *
                                    *********



        File name:      error.mac


        Usage

                error(format, arglist); /* Fatal error exit     */

        Description

                An  error  message  is written to stderr and the program
                exits.  If profiling  was  enabled,  a  subroutine  call
                trace will be written to stderr.  

                The exit status, $$exst, will be set to "error".  

        Diagnostics 

        Bugs 


[[        C Compiler and Library]]                                     Page 5-84
        exit    Exit from C programs


        5.70  Exit from C programs               ____ ____ _ ________



                                    ********
                                    * exit *
                                    ********



        File name:      exit.mac


        Usage

                exit(status);           /* Exit, no return      */

                exits(status);          /* Exit with status     */

                $$fail();               /* Immediate exit       */

                extern int $$exst;      /* Exit status value    */

          Internal

                jmp     $$exit          ;Call exit routine

        Description

                On exit, the following sequence occurs:  
                  1.    The user-supplied wrapup() function is called.
                  2.    User-supplied finalizers are called.
                  3.    Profiles (if requested) are printed.
                  4.    All files are closed.
                  5.    The program exits to the operating system.

                By  calling  exits()  with  an  appropriate  value,  the
                program can pass an exit status code  to  the  operating
                system monitor.  The RT11 and RSX11 monitors define exit
                status codes differently;  the value passed  to  exits()
                is not checked for consistancy.  

                  RT11  RSX     Meaning
                    1.   1.     IO_SUCCESS -- no message is printed
                    2.   0.     IO_WARNING -- minor error
                    4.   2.     IO_ERROR   -- serious error
                    8.   4.     IO_FATAL   -- severe error

                Calling  exit()  with  some other value is equivalent to
                calling exits(IO_SUCCESS).  This is compatible with Unix
                programs that exit by calling exit() without parameters. 

                Note  that  the program may also set a value into $$exst
                and exit via exit():  

[[        C Compiler and Library]]                                     Page 5-85
        exit    Exit from C programs



                        extern int $$exst;

                        ...

                        $$exst = IO_WARNING;
                        exit();

                If  the  program  calls,  or  jumps  to, $$fail, it will
                immediately exit to the operating system without closing
                files,  calling  wrapup()  or  finalizers,  or writing a
                profile file.  

        Diagnostics 

        Bugs 


[[        C Compiler and Library]]                                     Page 5-86
        fabs    Floating absolute value


        5.71  Floating absolute value               ________ ________ _____



                                    ********
                                    * fabs *
                                    ********



        File name:      fabs.mac


        Usage

                double
                fabs(val)
                double          val;

        Description

                Return absolute value of a floating argument.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-87
        fclear  Clear file error flags


        5.72  Clear file error flags               _____ ____ _____ _____



                                   **********
                                   * fclear *
                                   **********



        File name:      fclear.mac


        Usage

                fclear(iop);
                FILE            *iop;

        Description

                Clear  the  error  flags  for an open file.  This may be
                needed for interaction with the user's console terminal. 

        Bugs 


[[        C Compiler and Library]]                                     Page 5-88
        fclose  Close a currently-open file


        5.73  Close a currently-open file               _____ _ ______________ ____



                                   **********
                                   * fclose *
                                   **********



        File name:      fclose.mac


        Usage

                fclose(iop);
                FILE            *iop;

          Internal

                mov     #iov,r4         ;r4 -> i/o vector
                mov     <signal>,r0     ;r0 == 0 to free i/o vector
                call    $$clos          ;close file.

                mov     #iov,r4         ;r4 -> i/o vector
                mov     <signal>,r0     ;r0 == 0 to free i/o vector
                call    $$fcls          ;Free buffer space

        Description

                Close  the  file.  Returns 0 if ok, -1 if an error.  The
                error code is saved in $$ferr.  

                Note  that  stderr  is  never closed.  On RT11-mode, the
                last block of a disk file which was open for  output  is
                filled with nulls.  

        Internal 

                $$clos is called internally to close a file.  

                $$fcls is called internally to free buffer space.  

                After   the   file   has  been  closed,  record  buffers
                (RSX-mode) and the file-name buffer (RT11-mode) will  be
                freed.  

                If r0 is zero on entry, the iov and any wild-card buffer
                will also be  freed.   This  flag  is  set  non-zero  by
                freopen() or fnext() to close a file without freeing the
                iov.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-89
        feof    Test for end of file


        5.74  Test for end of file               ____ ___ ___ __ ____



                                    ********
                                    * feof *
                                    ********



        File name:      feof.mac


        Usage

                feof(iop);
                FILE            *iop;

        Description

                Return 1 if end of file on iop, else zero.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-90
        ferr    Test for file error


        5.75  Test for file error               ____ ___ ____ _____



                                    ********
                                    * ferr *
                                    ********



        File name:      ferr.mac


        Usage

                ferr(iop);
                FILE            *iop;

        Description

                Return  1  if  an  error  has been seen on the indicated
                file.  

        Bugs 

                Obsolete, use ferror() instead.  


[[        C Compiler and Library]]                                     Page 5-91
        ferror  Test for file error


        5.76  Test for file error               ____ ___ ____ _____



                                   **********
                                   * ferror *
                                   **********



        File name:      ferror.mac


        Usage

                ferror(iop);
                FILE            *iop;

        Description

                Return  1  if  an  error  has been seen on the indicated
                file.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-92
        fflush  Flush output buffers


        5.77  Flush output buffers               _____ ______ _______



                                   **********
                                   * fflush *
                                   **********



        File name:      fflush.mac


        Usage

                fflush(iop);
                FILE            *iop;

        Description

                Flush  output  buffers.  This routine actually does I/O.
                $$ferr is set if anything unexpected happens.  

        Bugs 


[[        C Compiler and Library]]                                     Page 5-93
        fget    Input a binary record


        5.78  Input a binary record               _____ _ ______ ______



                                    ********
                                    * fget *
                                    ********



        File name:      fget.mac


        Usage

                fget(buffer, maxbytes, iop);
                char            *buffer;
                int             maxbytes;
                FILE            *iop;

        Description

                Read  a record from the indicated file.  Maxbytes is the
                maximum record size.  

                On  RSX, the record is read by a direct call to the file
                service GET$ routine.  Your program must not  mix  calls
                to  fget()  with  calls  to  other I/O routines, such as
                fgets().  

                On RT11, the file must have been written by fput().  

                The actual number of bytes read is returned.  Use feof()
                to test for end of file.  

                Fget() is not present on Unix standard I/O libraries.  

        Internal 

                On  RT11,  when  the  record is written by fput(), it is
                preceeded by a two-byte byte count.  This value  is  one
                greater  than  the number of bytes in the record.  (If a
                zero count is read, it will mean "end of file.") 

        Bugs 


[[        C Compiler and Library]]                                     Page 5-94
        fgetname        Convert file name to Ascii


        5.79  Convert file name to Ascii               _______ ____ ____ __ _____



                                  ************
                                  * fgetname *
                                  ************



        File name:      fgetna.mac


        Usage

                char *
                fgetname(iop, buffer);
                FILE            *iop;
                char            *buffer;

        Description

                Convert the file name to Ascii and put it in the buffer. 

                On  native  RSX  (and RSTS/E emulation) the device name,
                file name, file  type,  and  version  are  converted  to
                Ascii.   The  UIC  is  converted if it was specified and
                differs from the job's default UIC.  (Note that  on  VMS
                compatibility mode, the UIC is unavailable.) The version
                is converted to octal on native RSX and  to  decimal  on
                VMS  emulation.   The  result  should  be  sufficient to
                delete the file.  

                On RT11 modes, the file name passed to fopen() is copied
                to the buffer without further processing.  If  the  file
                was  opened  by an fwild()/fnext() sequence, the correct
                file name is returned.  (On RSTS/E, the PPN is  returned
                as well.) 

                Fgetname() returns a pointer to the buffer argument.  

                Fgetname()  is  present in the Vax-11 C support library,
                but is not generally present on Unix implementations.  

                Note  that  fgetname()  returns  a  fully-qualified file
                specification  including,  where  possible,  the   disk,
                directory,  and  version  of  the  file.   The resulting
                string can be surprisingly long if using RMS and  DECnet
                (DAP) file names, logicals on P/OS, etc.  

                If  only  the  actual file name is needed, the following
                code segment may be executed.  As shown, it  writes  the
                file name and filetype (extension) to a global "buffer". 


[[        C Compiler and Library]]                                     Page 5-95
        fgetname        Convert file name to Ascii


                    getfilename(fd, buffer)
                    FILE                *fd;
                    register char       *buffer;
                    {
                        register char *tp;
                        register char c;

                        fgetname(fd, buffer);
                        /*
                         * Skip over node and device name
                         */
                        while ((tp = strchr(buffer, ':')) != NULL)
                            strcpy(buffer, tp + 1);
                        /*
                         * Skip over [UIC] or [PPN] if present
                         */
                        c = EOS;
                        switch (*tp) {
                        case '[':       c = ']'; break;
                        case '(':       c = ')'; break;
                        case '<':       c = '>'; break;
                        }
                        if (c != EOS
                         && (tp = strchr(buffer, c)) != NULL) {
                            strcpy(buffer, tp + 1);
                        /*
                         * Don't include version
                         */
                        if ((tp = strchr(buffer, ';')) != NULL)
                            *tp = EOS;
                    }

        Bugs

                Various operating systems behave differently.  


[[        C Compiler and Library]]                                     Page 5-96
        fgets   Read a string from a file


        5.80  Read a string from a file               ____ _ ______ ____ _ ____



                                    *********
                                    * fgets *
                                    *********



        File name:      fgets.mac


        Usage

                char *
                fgets(buffer, maxbytes, iop);
                char            *buffer;
                int             maxbytes;
                FILE            *iop;

                char *
                fgetss(buffer, maxbytes, iop);
                char            *buffer;
                int             maxbytes;
                FILE            *iop;

        Description

                Fgets()   reads  a  string  into  the  buffer  from  the
                indicated file.  Maxbytes is the maximum number of bytes
                to   read.   The  string  is  terminated  by  a  newline
                character,  which  is  followed  by  a  null.    Fgets()
                normally returns buffer.  It returns NULL on end of file
                or error.  If the line being read is  maxbytes  long  or
                longer, no newline is appended.  

                Fgetss()   is  identical  to  fgets()  except  that  the
                terminating newline is replaced by  a  null.   (This  is
                compatible  with  gets(), but fgetss() is not present in
                the Unix standard library.) 

                Note  that  fgets  keeps the newline, while fgetss() and
                gets() delete it.  To delete the newline after executing
                fgets(), execute the following:  

                        buffer[strlen(buffer) - 1] = 0;

        Bugs

                Note  that  fgets()  returns the next logical text line.
                Certain RSX-11 or  RMS  file  formats,  such  as  Runoff
                output  files  or  task-builder  load  maps,  often have
                multiple text lines  packed  into  one  logical  record.

[[        C Compiler and Library]]                                     Page 5-97
        fgets   Read a string from a file


                Fgets()  processes these correctly.  Note, however, that
                the record location, as  returned  by  ftell(),  is  the
                location  of  the  physical  record,  as returned by the
                operating system.  The "obvious" ftell/fgets sequence, 

                        rfa = ftell(fd);
                        fgets(text, sizeof text, fd);

                will not work properly if multiple text lines are packed
                into one RSX-11 record.  

                These  routines  do  not  understand  some  of  the more
                baroque RSX-11 file formats, such as  "Fortran  carriage
                control"  or VMS print-file format.  The typeout program
                in the tools package, T.C, shows an example of  complete
                record deblocking and "seek to byte" procedure.  


[[        C Compiler and Library]]                                     Page 5-98
        fileno  Get logical unit number


        5.81  Get logical unit number               ___ _______ ____ ______



                                   **********
                                   * fileno *
                                   **********



        File name:      fileno.mac


        Usage

                fileno(iop)
                FILE            *iop;

        Description

                Return the logical unit number associated with the file.
                (On RT11, the channel number is returned.) 

        Bugs 


[[        C Compiler and Library]]                                     Page 5-99
        fill    Fill a Block of Memory With a Character


        5.82  Fill a Block of Memory With a Character               ____ _ _____ __ ______ ____ _ _________



                                    ********
                                    * fill *
                                    ********



        File name:      fill.mac


        Usage

                fill(addr, ch, count);
                char            *addr;
                char            ch;
                unsigned int    count;

        Description:

                Fill  the  count  characters of memory beginning at addr
                with the character ch.  

                Note:   To  fill  with  zero  bytes, you can use zero(),
                which is slightly faster.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-100
        flun    Get logical unit number


        5.83  Get logical unit number               ___ _______ ____ ______



                                    ********
                                    * flun *
                                    ********



        File name:      flun.mac


        Usage

                flun(iop)
                FILE            *iop;

        Description

                Return the logical unit number associated with the file.
                (On RT11, the channel number is returned.) 

        Bugs 

                Obsolete -- use fileno() for transportability.  


[[        C Compiler and Library]]                                    Page 5-101
        fmkdl   Mark file for deletion -- obsolete


        5.84  Mark file for deletion -- obsolete               ____ ____ ___ ________ __ ________



                                    *********
                                    * fmkdl *
                                    *********



        File name:      fmkdl.mac


        Usage

                fmkdl(iop);
                FILE            *iop;

        Description


                fmkdl()  closes and deletes the specified file.  Returns
                0 on success, -1 on error.  

                This  routine  is  obsolete.   New  programs should call
                delete() instead.   To  delete  an  existing  file,  the
                program may execute:  

                        char    buffer[80];
                        ...
                        fgetname(iop, buffer);
                        fclose(iop);
                        delete(buffer);

        Bugs

                On RT11, the job is aborted with an error message if the
                file wouldn't parse.  $$ferr is set to "file not  found"
                if  the  program  tries  to  delete  something (like the
                line-printer) that it shouldn't.  Note  that  RT11  does
                not flush the last buffer before deleting the file.  

                On  VMS  compatibility  mode,  the  file  must be in the
                user's default directory.  


[[        C Compiler and Library]]                                    Page 5-102
        fopen   C library file opener


        5.85  C library file opener               _ _______ ____ ______



                                    *********
                                    * fopen *
                                    *********



        File name:      fopen.mac


        Usage

                FILE *
                fopen(name, mode);
                char            *name;  /* File to open         */
                char            *mode;  /* Open modes           */

                FILE *
                freopen(name, mode, iop);
                char            *name;  /* File to open         */
                char            *mode;  /* Open modes           */
                FILE            *iop;   /* I/O pointer          */

          Internal

                mov     iov,r4  ;r4 -> iov
                jmp     $$fopn  ;Open the file and return to the
                                ;caller via $$fopx or $$fope if error.
                                ;On RSX, fixup append mode if the file
                                ;wasn't found.

                mov     iov,r4  ;r4 -> iov
                call    $$fopo  ;Normal open, then exit via $$fopx
                                ;On RSX, $$fopo returns if any error
                                ;occurred. On return, r0 := RSX error
                code.

                mov     iov,r4  ;r4 -> iov, file is open
                jmp     $$fopx  ;Normal exit from fopen
                                ;On RSX, $$fopx allocates the record
                                ;buffer.

                mov     iov,r4  ;r4 -> iov (or r4 == 0)
                mov     code,r0 ;r0 := error code (to go to $$ferr)
                jmp     $$fope  ;Error exit from fopen
                                ;$$fope deallocates buffers

        Description

                Fopen  opens  a  new  or  existing file in the indicated
                mode:  

[[        C Compiler and Library]]                                    Page 5-103
        fopen   C library file opener



                        r       Read the existing file sequentially
                        w       Create and write the file sequentially
                        a       Append to the file
                        n       Not record oriented
                        u       RSX-mode "unbuffered i/o"
                                RT11-mode: use .ttyin and .ttyout


                Either  "r", "w", or "a" must be given.  "n" and "u" are
                optional.  "n" should be given for "binary" files.  Note
                that  "n"  mode  will  create fixed-block records on RSX
                systems.  Append mode does not work on native RT11.  

                Note that "n" and "u" are not compatible with other Unix
                systems.  

        Implementation Details 

                On  RSX,  "u"  mode  files  will  be  created  with  the
                "variable-length"  attribute.   On  RSTS/RSX  emulation,
                text  files  (neither  "n"  nor  "u"  specified) will be
                created with "stream" attribute.  

                On  RSX, if the record type bits in the record attribute
                byte (F.RATT in the FDB) is zero, the file will be  read
                as  if  the  "n"  was specified.  Note that, if the file
                contains carriage-return line-feed sequences, the entire
                sequence  will  be  passed  to  the  user's program.  If
                record    attributes     are     understandable,     the
                carriage-return will be deleted from <CR><LF> sequences. 

                On  RSX,  if the "file" is being opened for write to the
                same  device/unit  as  stderr   (the   user's   "command
                console),  the  character  stream is diverted to stderr.
                This avoids synchronization problems by  funnelling  all
                output  through the same buffer.  In addition, output to
                any terminal device is done via QIO's to  the  terminal,
                IO.WLB for normal mode, IO.WAL for "n" mode.  

                On  RT11,  when  opening  a file for writing, a specific
                block allocation may  be  included  in  the  Ascii  file
                specification    following    standard   RT-11   syntax:
                "DKn:file.nam[nnn]" where the "nnn" specifies the number
                of blocks to allocate to the file.  After opening a file
                successfully, the actual file size (or number of  blocks
                allocated) will be found in (FILE *)fd->io_size.  

                If  the RT11 library decides that the file is really the
                user's command terminal, single-character  I/O  will  be
                performed  (by  calling  .ttyin and .ttyout).  Note that
                the "special-mode" bits must be set in  the  Job  Status
                Word by the program if it requires true single-character
                or immediate return input.  Output to the terminal  will

[[        C Compiler and Library]]                                    Page 5-104
        fopen   C library file opener


                be  performed  without  buffering,  which  is useful for
                screen updating, but otherwise expensive.  

                Fopen()  returns  NULL on errors -- $$ferr gets an error
                code.  On RT11, this will be a  RSTS/E  compatible  code
                (described  in  iov), while on RSX, this will be the FCS
                error code.  

                On RT11, the file name pointed to by the "io_name" field
                of the iov is either the file name string as  passed  to
                fopen() or an ascii string reconstructed from the 4-word
                Rad50 device block if the file was opened as part  of  a
                fwild/fnext  sequence.   By  saving  the  ascii  string,
                RSTS/E is able to  re-parse  logical  device  names  and
                PPN's, which are not present on native RT11.  

                On  VMS  compatibility mode, the device and directory of
                the file name argument are saved in the  iov  "io_dname"
                field for use by fgetname().  

                Note that "no buffer space available" (IE.NBF or E$$NSP)
                and "invalid lun" (IE.ILU or E$$NOC) may be generated by
                fopen.   On  RT11,  if the file cannot be opened because
                the user's program has already opened  the  channel,  an
                E$$ILU error will be returned.  

                The  same  file  may  not  be  used for both reading and
                writing except if the program writes a disk  file,  then
                repositions and reads it using ftell()/fseek().  In this
                case, the program should call rewind() or  freopen()  to
                reinitialize the file before using fseek().  

                Except  in  the  one  specific  case of the RT11 console
                terminal open in "u" mode, an open file must not be used
                for reading and writing at the same time.  

                Freopen()  substitutes  the  named  file in place of the
                open file -- indicated by iop.  The file currently  open
                on  iop  is  closed.   Freopen returns iop.  If the open
                failed, iop will  be  deallocated.   Note  that  freopen
                loses any pending fwild/fnext status.  


        Internal 

                The   following   routines/globals   are   for   use  by
                fopen/fwild.  If any of these routines detect an  error,
                they  return  to  the fopen() caller with an appropriate
                error code in $$ferr.  

                        $$fope          Error exit from fopen
                        $$fopn          Normal open, hack append
                        $$fopx          Normal exit from fopen


[[        C Compiler and Library]]                                    Page 5-105
        fopen   C library file opener


                Warning:   fopen()  in  RSX/RSTS  mode  uses unpublished
                information to obtain the PPN [UIC]  of  an  open  file.
                This  code  (in  iocsi.mac) may require modification for
                subsequent releases of RSTS/E.  

        Bugs 

                Append  mode cannot work on native RT11 given the design
                of the RT11 file system.  

                The RT11 file system does not support files greater than
                65535 blocks long.  

                RT11  does  not  get  the  actual  keyboard  name of the
                console terminal, although this isn't too hard to do  on
                RT11/RSTS/E.  

                Freopen()  cannot  be used to assign a file to stderr as
                there is code throughout the  i/o  package  for  special
                treatment  of  stderr.  For example, it cannot be closed
                by a user-written program.  

                In  RSX  modes,  the maximum number of files that may be
                simultaneously open is defined at  assembly  time  by  a
                macro  (FSRSZ$)  which  is  expanded  when  fopen.mac is
                assembled.  The default FSRSZ$ parameter is 4.  This may
                be  modified by using the task builder /ACTFIL=n option.
                The default FSRSZ$ value may be specified when  the  RSX
                library is built by editing assembly parameter N$$FIL in
                RSX.MAC.  

        Internal 

                This  module contains release-specific code for VMS V3.0
                to enable Decus C programs to read "Ascii stream" files. 


[[        C Compiler and Library]]                                    Page 5-106
        fprintf Formatted Output Conversion


        5.86  Formatted Output Conversion               _________ ______ __________



                                   ***********
                                   * fprintf *
                                   ***********



        File name:      fprint.mac


        Usage

                fprintf(iov, format, arg1, ...);
                FILE            *iov;
                char            *buffer;
                char            *format;

        Description

                fprintf()  converts  and  formats its arguments, writing
                the result to the indicated file.  

                For  information  on  formatting,  please  refer  to the
                description of printf.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-107
        fps     Set floating point status (FPS)


        5.87  Set floating point status (FPS)               ___ ________ _____ ______ _____



                                     *******
                                     * fps *
                                     *******



        File name:      fps.mac


        Usage

                #include <fps.h>

                fps(status)
                unsigned int    status;

        Description

                This  routien  sets  the floating point status by simply
                executing the LDFPS instruction.   This  allows  a  user
                program  to switch between roundoff and truncation modes
                or  enable/disable  floating  point   interrupts.    Bit
                definitions are in the include file, "fps.h".  

                For  example,  to  enable  rounding  and  all  fpu error
                interrupts except underflow, do the following:  

                        #include <fps.h>
                        fps(FIUV | FIV | FIC);

        Bugs

                The  C  library  doesn't  initialize  the floating point
                status.  This routine -- with appropriate parameters  --
                should  be  in all C main programs that require floating
                point operations.  


[[        C Compiler and Library]]                                    Page 5-108
        fput    Output a binary record


        5.88  Output a binary record               ______ _ ______ ______



                                    ********
                                    * fput *
                                    ********



        File name:      fput.mac


        Usage

                fput(buffer, nbytes, iop);
                char            *buffer;
                int             nbytes;
                FILE            *iop;

        Description

                The  specified  record is written to the file.  The file
                must have been opened 'n'  so  newlines  aren't  stuffed
                here and there.  

                On RT11, the file is only readable by fget.  

                Nbytes is always returned.  

                A call to ferr() after calling fput() is advised.  

        Bugs 

                On  RT11, file close zeros the current output block.  To
                prevent fget() from reading "zero length" records,  fput
                writes "record count + 1" on the file.  


[[        C Compiler and Library]]                                    Page 5-109
        fread   Input a record


        5.89  Input a record               _____ _ ______



                                    *********
                                    * fread *
                                    *********



        File name:      fread.mac


        Usage

                int
                fread(object, sizeof (*object), nitem, iop)
                int             nitem;
                FILE            *iop;

        Description

                Object points to a buffer that is to receive a specified
                number of items from the file.  

                fread()  returns  the actual number of items read.  This
                will be zero if an end-of-file or error was encountered. 

        Bugs 


[[        C Compiler and Library]]                                    Page 5-110
        frec    Return True if record-oriented file


        5.90  Return True if record-oriented file               ______ ____ __ _______________ ____



                                    ********
                                    * frec *
                                    ********



        File name:      frec.mac


        Usage

                frec(iop);
                FILE            *iop;

        Description

                Return 1 if the file is record-oriented.  Note:  in this
                context, record-oriented files are  not  file-structured
                disks,  nor are they the user's console terminal.  Other
                terminals, along with  devices  such  as  line-printers,
                qualify, however.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-111
        fscanf  Formatted input conversion


        5.91  Formatted input conversion               _________ _____ __________



                                   **********
                                   * fscanf *
                                   **********



        File name:      fscanf.mac


        Usage

                fscanf(fd, fmt, pointer(s))
                FILE            *fd;    /* Input file pointer   */
                char            *fmt;   /* Format string        */

        Description

                Fscanf()   parses   the  input  file  according  to  the
                indicated format descriptor, storing the results in  the
                pointer   arguments.    It   returns   the   number   of
                successfully assigned input items.  

                See    the    description   of   scanf()   for   further
                documentation.  

        Diagnostics 

                Fscanf()  returns  -1 if an end of file condition exists
                and no data was stored.  It returns  -2  if  a  palpably
                incorrect format, such as "%" is encountered.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-112
        fseek   Reposition file pointer (seek)


        5.92  Reposition file pointer (seek)               __________ ____ _______ ______



                                    *********
                                    * fseek *
                                    *********



        File name:      fseek.mac


        Usage

                fseek(iop, offset, param);
                FILE            *iop;   /* What device to seek  */
                long            offset; /* New read position    */
                int             param;  /* Zero for abs. seek   */

        Description

                fseek()   moves   the  file  pointer  to  the  indicated
                position.  The  position  must  have  been  returned  by
                ftell()  or  equal zero for rewind.  Param must be zero.
                The file/device must be seekable.  

                fseek() returns zero if correct, EOF if an error occurs.
                If no error occurred, error and eof flags are reset.  

                flseek() is an alternate entry with identical parameters
                and actions.  

                Note that on RSX, fseek() can be used to open a file for
                update by a sequence such as:  

                        fd = fopen("file.nam", "a");
                        fseek(fd, 0L, 0);       /* Rewind file  */

                If the file was opened on RSX using the 'n' mode switch,
                it will be opened using file attributes "fixed  512-byte
                records  with  no carriage control".  The offset pointer
                is thus a virtual byte number and fseek may be  used  to
                freely reposition the file pointer.  

        Bugs  For  RMS-11  versions,  the  sequence  fseek() followed by
                ftell() on the same file, with no intervening  reads  or
                writes,  will  advance the position one record.  This is
                an unfortunate  side-effect  of  the  positioning  hacks
                required  to  make  the well-behaved RMS "look" like the
                crude UNIX positioning.  


[[        C Compiler and Library]]                                    Page 5-113
        fspool  Spool file to default print queue


        5.93  Spool file to default print queue               _____ ____ __ _______ _____ _____



                                   **********
                                   * fspool *
                                   **********



        File name:      fspool.mac


        Usage

                fspool(fp);
                FILE            *fp;    /* Open file IOV        */

        Description

                This  routine  is  called in lieu of fclose() when it is
                desired to spool the file to the  system  line  printer.
                There  is  no  control  over the disposition or printout
                parameters.  

                Fspool()  returns  zero  if  the  file  was  spooled, it
                returns  an  error  code  if  spooling  could   not   be
                initiated.   If  called on native RT11, the file will be
                closed and an "illegal device error" (E$$NOD =  6)  will
                be returned.  

                If  the  program  needs access to the power of the queue
                manager print spooler on native RSX, the RSX  extensions
                library spwn() routine should be used to spawn a command
                line to MCR after closing the file as usual.  

                If  the  program  needs access to the power of the queue
                manager on RSTS/E, it should close the file and use  the
                routines in the RSTS/E extensions library to execute the
                UU.SPL system function call.  

                On  RSTS/E V7.0, the file is spooled to any line printer
                (RSX mode) or to LP0:  in  RT11  mode.   The  particular
                line  printer  cannot  be selected without modifying the
                source of fspool().  

                If  the  file  was  opened  by  calling fwild()/fnext(),
                internal buffers will not be freed, allowing the program
                to call fnext() for subsequent files.  

        Bugs 

                On  RSTS/E  RT11  mode,  error  codes  will  follow  the
                description of the spooling system function call.  

[[        C Compiler and Library]]                                    Page 5-114
        fspool  Spool file to default print queue




[[        C Compiler and Library]]                                    Page 5-115
        ftell   Get file position for subsequent seek


        5.94  Get file position for subsequent seek               ___ ____ ________ ___ __________ ____



                                    *********
                                    * ftell *
                                    *********



        File name:      ftell.mac


        Usage

                long
                ftell(iop);
                FILE            *iop;   /* What device to seek  */

        Description

                ftell()  returns  the position of the read/write pointer
                of the indicated file.  This value may be  fed  back  to
                the file system by calling fseek().  Note that the value
                is a pointer to the record, not a block or byte pointer.
                On  RSX,  the  program  should  flush the current record
                before calling ftell().  (Flush() is a noop on RT11.) 

                If reading lines of text, the correct sequence is:  

                        position = ftell(fd);
                        if (fgets(buffer, sizeof buffer, fd) != EOF) {
                                /*
                                 * 'position' locates the record
                                 * read by the call to fgets()
                                 */
                        }

                Make sure you declare ftell() 

                        extern long ftell();

                If you do not, it will return garbage.  

        Bugs 

                On  both  systems, the value returned is the position of
                the file pointer (RFA), as a byte offset from the  start
                of  the  file.   Note,  however, that on RSX systems the
                pointer is to the start of the current  record.   It  is
                not  necessarily  the case that the start of a text line
                equates to the start of a  record.   RSX  supports  many
                file  record  formats, including Fortran, print_file and
                "unformatted" (with embedded control information).   The

[[        C Compiler and Library]]                                    Page 5-116
        ftell   Get file position for subsequent seek


                latter  files  may  have multiple text lines embedded in
                each  record.   This  is  handled  internally   by   the
                formatted  read routines (i.e., fgets() and getc()).  On
                RSX, the only way to be certain of the exact record/line
                correspondance   is   to   use  the  fget()  and  fput()
                functions.  The T utility program (in the tools library)
                shows another method of handling this problem.  

                On  RSTS/E  RT11  mode,  ftell  will not process "large"
                files (with more than 65535 blocks) correctly.  

                For  RMS-11  versions,  the sequence fseek() followed by
                ftell() on the same file, with no intervening  reads  or
                writes,  will  advance the position one record.  This is
                an unfortunate  side-effect  of  the  positioning  hacks
                required  to  make  the well-behaved RMS "look" like the
                crude UNIX positioning.  


[[        C Compiler and Library]]                                    Page 5-117
        ftime   Compute time of day (augmented)


        5.95  Compute time of day (augmented)               _______ ____ __ ___ ___________



                                    *********
                                    * ftime *
                                    *********



        File name:      ftime.mac


        Usage


                #ifdef unix
                #include <sys/types.h>
                #include <sys/timeb.h>
                #else
                #include <timeb.h>
                #endif

                long
                ftime(buf);
                struct timeb    *buf;

        Description

                ftime  returns  the  time  of  day in seconds.  The time
                buffer receives the time of day, milliseconds since  the
                current  second,  and timezone and Daylight Savings time
                indicators.  

                The time buffer has the following format:  

                  struct timeb {
                    long      time;     /* Time of day          */
                    unsigned  millitm;  /* Milliseconds         */
                    short     timezone; /* Current timezone     */
                    short     dstflag;  /* Daylight Savings     */
                };  

                The  time  value is the time since midnite, Jan 1, 1970,
                measured in seconds.  The timezone value is  the  number
                of minutes that local time differs from GMT.  

                Note that, on Unix, the time buffer definition is stored
                in the sys directory, while for Decus-C and Vax-11 C, it
                is   stored  in  the  default  system  library  (C:   or
                sys$library:  respectively).  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-118
        ftime   Compute time of day (augmented)


                The  Unix  time  function  returns GMT.  Decus C returns
                local time.  Timezone and dstflag are set to zero.  


[[        C Compiler and Library]]                                    Page 5-119
        ftty    Test if terminal file


        5.96  Test if terminal file               ____ __ ________ ____



                                    ********
                                    * ftty *
                                    ********



        File name:      ftty.mac


        Usage

                ftty(iop)
                FILE            *iop;

        Description

                Return  1  if  the  file  is a terminal-type device.  In
                general, this means the user's command terminal.  

        Bugs 

                Obsolete   --   use   isatty(fileno(iop))   instead  for
                transportability.  


[[        C Compiler and Library]]                                    Page 5-120
        fwild   Wild-card file open


        5.97  Wild-card file open               _________ ____ ____



                                    *********
                                    * fwild *
                                    *********



        File name:      fwild.mac


        Usage

                FILE *
                fwild(name, mode);
                char            *name;  /* File to open         */
                char            *mode;  /* Open modes           */

                FILE *
                fnext(iop);
                FILE            *iop;   /* I/O pointer          */

        Description

                Fwild()  opens  a  new or existing file (whose file name
                may contain "wild-cards").  Open modes are identical  to
                those  given  in  fopen().  On return, the file name has
                been parsed, but no file has yet been  opened.   A  NULL
                return means that the file name did not parse correctly. 

                Fnext()  opens  the first or next file which was defined
                by a previous call to fwild().  If fnext() returns NULL,
                there  are  no  (more)  files  that  match the wild-card
                specification.  

                fwild/fnext handle RSX file version numbers correctly on
                VMS  compatibility  mode  (which  uses  the  ODS2   disk
                structure).   Fwild/fnext  do not handle version numbers
                correctly on native RSX systems which use  the  FILES-11
                (ODS1)  disk  structure.   For  example,  a  program can
                request "foo.*;3", "foo.*;*", "foo.*;0", and "foo.*;-1".
                Omitting  a  version  number  "foo.*"  is  equivalent to
                "foo.*;0".   Note  that  version  number  0  means   the
                "newest" file, while version number -1 means the oldest.
                (Version numbers are not used on RT11 or RSTS/E.) 

                For   native   RSX  systems  (using  the  FILES-11  disk
                structure), an explicit version number and the  wildcard
                version number work correctly.  Version numbers 0 and -1
                work only if the directory has been reorganized by using
                the  SRD utility program.  If the directory has not been
                reorganized (such  that  the  youngest  version  appears

[[        C Compiler and Library]]                                    Page 5-121
        fwild   Wild-card file open


                first    in   the   directory),   fnext()   will   yield
                unpredictable results.  

                On   RT-11,  the  wildcard  filename  match  is  handled
                internally  to  fwild/fnext.   The  parser  will  handle
                several forms of wild file specs, including imbedded '*'
                and the single character wildcard '%', and acts the same
                as  the  DIRECTORY wildcard handler.  For convenience, a
                '?' acts the same as a '%' in a match string.  

                Note:   if  a  program  executes fclose(), all file name
                information  will  be  lost.   The  following   sequence
                illustrates proper use of fwild()/fnext():  

                        if (gets(name_buff) == NULL)
                                exit();
                        if ((fd = fwild(name_buff, "r")) == NULL)
                                error("Can't open %s\n", name_buff);
                        for (count = 0; fnext(fd) != NULL; count++) {
                                /*
                                 * Process each file
                                 */
                                while (fgets(buffer, sizeof buffer, fd)
                                                != NULL) {
                                        /*
                                         * Process each record
                                         */
                                }
                        }
                        /*
                         * fnext() fails; the channel is closed.
                         * count has the number of files processed.
                         */
                        if (count == 0)
                                error("No matching files found");

                The   following   summarizes   the  types  of  wild-card
                processing available on the various  implementations  of
                the C support library:  

                   Environment  Supports

                   Native RSX   "*"  matches  any filename, filetype, or
                                version number.  Version ;0 and ;-1  are
                                supported on ODS2  systems.   UIC's  may
                                not contain wildcards.

                   RSX/VMS      As above, note that  version  ;-1  means
                                the "earliest"  version.   Note  warning
                                below.  Directory identifiers may not be
                                wildcarded.  VMS systems support ODS2.

                   RSX/RSTS     Uses RSTS/E  wildcard  conventions:  "*"
                                replaces   filename  or  filetype.   "?"

[[        C Compiler and Library]]                                    Page 5-122
        fwild   Wild-card file open


                                matches any character.  PPN's may not be
                                wildcarded.   Version  numbers  are  not
                                supported on RSTS/E.

                   Native RT11  "*" replaces  any  string,  "%"  or  "?"
                                match any non-blank character.

                   RT11/RSTS    Uses RSTS/E wildcard  conventions  noted
                                above.

        Bugs

                On   native  RSX  systems  using  ODS1  (FILES-11)  disk
                structures, version numbers will be  processed  properly
                only  if  directories have been sorted (by using the SRD
                utility program, for example).  If directories  are  not
                sorted, and fwild() is invoked with version number ;0 or
                ;-1, it will yield unpredictable results.  

                The  command  language scan (CSI1$) on VMS compatibility
                mode does not parse version number -1 (because it has  a
                different  meaning  on  native  VMS)  and  fwild()  will
                consequently fail.  

                If  you  want  the  oldest  version,  fwild()  should be
                invoked  with  a  file  name  of  the  type  "foo.*"  or
                "foo.*;0"  and,  before  calling  fnext()  for the first
                time, you should set the correct bits in  the  IOV  flag
                word as follows:  

                        if ((fd = fwild(file, "r")) == NULL)
                                error("can't open file %s", file);
                        if ((fd->io_flag & IO_VER) != 0
                                        && version_minus_1_wanted)
                                fd->io_flag |= IO_VM1;

                Flag  bit  IO_VER  signals  "version 0 or -1", while bit
                IO_VM1 signals version minus 1.  Again, note  that  this
                must be done before the first call to fnext().  

                On  native  RT11  and all RSTS/E modes, fwild/fnext will
                fail if the device is not directory structured (even  if
                no  wildcard  file is specified).  If this is a problem,
                you should write:  

                        if ((fd = fwild(filename, mode)) != NULL)
                                iswild = 1;
                        else if ((fd = fopen(filename, mode) != NULL)
                                iswild = 0;
                        else error("cannot open the file");

                The  program  must  then  test iswild to determine if it
                must call fnext() or if processing should  be  initiated
                directly.  

[[        C Compiler and Library]]                                    Page 5-123
        fwild   Wild-card file open



                On  all RSTS/E modes, there may be problems with logical
                name translation as file name  strings  must  be  parsed
                more  than once.  Thus, if a programer defines a logical
                name which is identical to a valid physical device name,
                a  wildcard  lookup  may  access  the  wrong unit.  This
                problem is described in the RSTS/E documentation.  

                Fwild/fnext was designed to work only with disk devices.
                It  will  not  necessarily  work  correctly  with  other
                directory-structured devices, such as magtape.  

        Internal 

                If  you  are always running on RSTS/E, or always running
                on RSX-11 (native or VMS compatibility mode)  or  always
                running  on  native  RT11,  you  should consider editing
                fwild.mac to remove unnecessary code.  

                This  routine  depends  on some internal knowledge about
                RSTS/E and  about  the  implementation  of  RSX-11  file
                control  services  on  RSTS/E.  It may need modification
                for subsequent releases of RSTS/E.  

                The  implementors  do not apologize for the size of this
                module.  

                The  distribution  of  the  C  language  system includes
                source code  for  the  SRD  (sort  directories)  utility
                program.  


[[        C Compiler and Library]]                                    Page 5-124
        fwrite  Output a record


        5.98  Output a record               ______ _ ______



                                   **********
                                   * fwrite *
                                   **********



        File name:      fwrite.mac


        Usage

                int
                fwrite(object, sizeof (*object), nitem, iop)
                int             nitem;
                FILE            *iop;

        Description

                Object  points  to a buffer that is contains a specified
                number of items to be written to the file.  

                fwrite()  returns  the  actual  number of items written.
                This will be zero if an error was encountered.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-125
        getchar Get characters


        5.99  Get characters               ___ __________



                                   ***********
                                   * getchar *
                                   ***********



        File name:      getcha.mac


        Usage

                getchar();

                getc(iop);
                FILE            *iop;

        Description

                Getchar()  reads  one  character from the standard input
                file.  getc() reads one  character  from  the  indicated
                input file.  

                Both return EOF on error or end of file.  

                To  continue  reading  from  a  terminal  after EOF, the
                program may execute:  

                        clearerr(iop);

        Bugs


[[        C Compiler and Library]]                                    Page 5-126
        gets    Read a string from stdin


        5.100  Read a string from stdin                ____ _ ______ ____ _____



                                    ********
                                    * gets *
                                    ********



        File name:      gets.mac


        Usage

                char *
                gets(buffer);
                char            *buffer;

        Description

                gets()  reads a string into the buffer from the standard
                input (stdin).  The string is terminated  by  a  newline
                character,  which  is  replaced in the buffer by a null.
                Gets() returns buffer or NULL on end of file or error.  


        Bugs 


[[        C Compiler and Library]]                                    Page 5-127
        gettty  Get control terminal name


        5.101  Get control terminal name                ___ _______ ________ ____



                                   **********
                                   * gettty *
                                   **********



        File name:      gettty.mac


        Usage

                gettty(buffer);
                char            *buffer;

        Description

                Store  the  device  name  of the control terminal in the
                buffer.  If this cannot be done, a null string  will  be
                returned.  

        Bugs 

                On   RSX   modes,  gettty()  uses  the  GLUN$  executive
                directive to obtain the device name and unit  number  of
                stderr   (which   always  is  assigned  to  the  control
                terminal).  

                On  RT11 modes, gettty() calls iovtoa to return the file
                name  on  which  stderr  was  opened.   This  will   not
                necessarily contain a valid unit number.  


[[        C Compiler and Library]]                                    Page 5-128
        getw    Input a binary integer from a file


        5.102  Input a binary integer from a file                _____ _ ______ _______ ____ _ ____



                                    ********
                                    * getw *
                                    ********



        File name:      getw.mac


        Usage

                getw(iop);
                FILE            *iop;

        Description

                getw()  reads one (16-bit) word from the indicated file.
                The program must call feof() or ferr() to test  for  end
                of file or error.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-129
        inchr   Find Index of Character in a String


        5.103  Find Index of Character in a String                ____ _____ __ _________ __ _ ______



                                    *********
                                    * inchr *
                                    *********



        File name:      inchr.mac


        Usage

                char *
                inchr(stng, chr)
                char            *stng;  /* String to search in  */
                char            chr;    /* Byte to search for   */

        Description

                If chr is in stng, return its index, i.e.  the offset in
                bytes   from   the   beginning   of   the    string    -
                inchr("abc",'b')  ==  1.   If chr is not in stng, return
                -1.  

                See also strchr().  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-130
        index   Find First Instance of a Character in a String


        5.104  Find First Instance of a Character in a String                ____ _____ ________ __ _ _________ __ _ ______



                                    *********
                                    * index *
                                    *********



        File name:      index.mac


        Usage

                char *
                index(stng, chr)
                char            *stng;  /* String to search in  */
                char            chr;    /* Byte to search for   */

        Description

                If  chr  is  in  stng,  return a pointer to it.  If not,
                return NULL.  

        Bugs 

                Obsolete;  use strchr() instead.  


[[        C Compiler and Library]]                                    Page 5-131
        iov     I/O vector definition


        5.105  I/O vector definition                ___ ______ __________



                                     *******
                                     * iov *
                                     *******



        File name:      iov.mac


        Usage

                #include <stdio.h>

                ... to be supplied ...

             Bits in iov.io_flag:

                #define _IOREAD 0000001 /* read                 */
                #define _IOWRT  0000002 /* write                */
                #define _IONBF  0000004 /* Unbuffered, "u" mode */
                #define _IOMYBUF 000010 /* I/O lib. owns buffer */
                #define _IOEOF  0000020 /* End of file seen     */
                #define _IOERR  0000040 /* Error seen           */
                #define _IOSTRG 0000100 /* For sprintf          */
                #define _IORW   0000200 /* Open for read/write  */
                #define IO_CMD  0000400 /* User's command titty */
                #define IO_APN  0001000 /* Append mode open     */
                #define IO_NOS  0002000 /* No newlines needed   */
                #define IO_NEWL 0004000 /* RSX TTY newline hack */
                #define IO_FIL  0010000 /* Disk file            */
                #define IO_TTY  0020000 /* Terminal device      */
                #define IO_REC  0040000 /* Record device        */
                #define IO_OPN  0100000 /* Open file            */
                #define IO_EOR  (IO_ERR | IO_EOF)

             Bits in iov.io_wflag:
                #define IO_WLD  0000001 /* fwild: wildcard file */
                #define IO_VM1  0000002 /* fwild: version ;-1   */
                #define IO_VER  0000004 /* fwild: ;0 or ;-1     */
                #define IO_WF1  0000010 /* fwild first flag     */
                #define IO_NLH  0000020 /* Newlines hack bit    */

             Bits in iov.io_rsflag (RSTS native only)
                #define IO_ODT2 0100000 /* ODT mode (RSTS only) */

                extern int   $$ferr;    /* Error word           */
                extern FILE  *stdin;    /* Standard input  file */
                extern FILE  *stdout;   /* Standard output file */
                extern FILE  *stderr;   /* User's command tty   */
                extern int   $$exst;    /* Exit status          */

[[        C Compiler and Library]]                                    Page 5-132
        iov     I/O vector definition



          Internal

                extern FILE  *$$luns[]; /* IOV pointer table    */
                extern FILE  *$$lune;   /* IOV table end        */
                extern (int)(char *$$lmax); /* RSX $$luns dim.  */
                extern char  **$$ifil;  /* -> stdin file name   */
                extern char  **$$ofil;  /* -> stdout file name  */
                extern int   $$nlun;    /* RSX: Number of luns  */
                FILE         *$$eiov;   /* RSX: Stderr iov      */
                extern int   $$iosb[2]; /* RSX: I/O status      */

        Description

                Define  the  I/O vector structure used for communication
                by all I/O routines in the C library.  Note that  it  is
                different  for  RSX  and  RT11  modes.   Note  also that
                certain bits in IO_FLAG  are  only  meaningful  for  one
                flavor of I/O.  

                The  RSX-mode  IOV  contains  an  entire file data block
                (FDB).  Also, 'io_uic' contains the binary  UIC  of  the
                directory  via which the file is being accessed, not the
                'owner' UIC.   It  is  this  UIC  which  is  given  when
                fgetname() is called.  

                The  RT11-mode  IOV  contains only enough information to
                read and write files plus a pointer to an  Ascii  string
                with  the  file name argument to fopen().  The file name
                is needed for fgetname() and  to  allow  deleting  files
                given the IOV pointer.  

                The following files are defined here:  

                        stdin   The standard input file.

                        stdout  The standard output file.

                        stderr  The error  output  file.   Note:  on RSX
                                systems, stderr is opened on LUN 1.

                $$ferr  (error  word) is also defined here.  This is set
                non-zero if an error occurred when performing  I/O.   On
                RSX,  the standard I/O error code is returned.  On RT11,
                an error code compatible with RSTS/E usage is returned: 

                        Global   Value  Meaning
                        E$$ILF  02. 002 Illegal file name
                        E$$NOR  04. 004 No room for user on device
                        E$$FNF  05. 005 Can't find file or account
                        E$$NOD  06. 006 Not a valid device
                        E$$ILU  07. 007 I/O channel in use
                        E$$NOO  09. 011 I/O channel not open
                        E$$EOF  11. 013 End of file on device

[[        C Compiler and Library]]                                    Page 5-133
        iov     I/O vector definition


                        E$$FAT  12. 014 Fatal system I/O failure
                        E$$ERR  13. 015 User data error on device
                        E$$FND  16. 020 File already found (protected)
                        E$$NOC  17. 021 Too many open files on unit.
                        E$$NSP  32. 040 No memory space for buffer

                E$$FAT (12) is set only if an "impossible" error occurs.
                While this may indicate a bug in the RT11 library, it is
                more likely to be a user programming error (like passing
                garbage to an I/O routine).  

                E$$ILU  (7) is set if fopen tries to open a channel that
                is already in use.  

                The  perror()  library  routine  may be used to print an
                error message defined for the error code.  

                $$exst  (exit  status) is used to transmit a termination
                code to the operating  system.   The  value  is  set  by
                calling  exit()  or  exits().  The following exit status
                values are defined in stdio.h:  

                  Global  #define    RSX RT11 Meaning
                  E$$XOK IO_SUCCESS   1    1  Normal
                  E$$XWA IO_WARNING   0    2  Warning
                  E$$XER IO_ERROR     2    4  Error
                  E$$XFA IO_FATAL     4    8  Severe Error

        Internal

                In  RSX,  buffering  is  done by the RSX file-management
                services (FCS).  The block buffer pointer is unused (but
                reserved for anybody who cares to add random access).  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-134
        irand   Random number modulus argument


        5.106  Random number modulus argument                ______ ______ _______ ________



                                    *********
                                    * irand *
                                    *********



        File name:      irand.mac


        Usage

                int
                irand(arg)
                int             arg;

        Description

                Generate  a  pseudorandom  number  in  the  range  0  ..
                (arg-1).  If arg is zero, generate a number in the range
                0 ..  32767.  

                Note  that the algorithm is prone to nonrandom sequences
                when considering the next pseudorandom number.  

                irand is equivalent to the following sequence:  

                        extern long     rand;

                        if (arg == 0) arg = 32767;
                        return(((rand() >> 8) & 32767) % arg);

        Bugs


[[        C Compiler and Library]]                                    Page 5-135
        isalloc Check If a Pointer Points to Allocated Memory


        5.107  Check If a Pointer Points to Allocated Memory                _____ __ _ _______ ______ __ _________ ______



                                   ***********
                                   * isalloc *
                                   ***********



        File name:      isallo.mac


        Usage

                int
                isalloc(buff)
                char *buff;

        Description

                isalloc()  returns  1 if buff is a pointer to a block of
                memory allocated by  calloc(),  malloc(),  or  realloc()
                that  has  not  been  freed  (by free());  -1 if it is a
                (recently) freed allocated block;  and 0 otherwise.  

                isalloc(NULL) == 0.  

                isalloc(p)  will  remain  -1  after a call of free(p) at
                least until the next call to  calloc(),  malloc(),  etc.
                Beyond that, its value is not predictable.  Pointers for
                which isalloc() is non-zero are exactly those  that  may
                safely be passed to realloc().  

                The  test  done  by  isalloc() is definitive, unlike the
                tests done by, for example, free()  and  msize(),  which
                will  yield  false  positives  at least 25% of the time.
                However, isalloc() is slower.  

        Bugs 

                Not portable.  

[[        C Compiler and Library]]                                    Page 5-136
        isalnum Return TRUE if Upper-case alphanumeric argument


        5.108  Return TRUE if Upper-case alphanumeric argument                ______ ____ __ __________ ____________ ________



                                   ***********
                                   * isalnum *
                                   ***********



        File name:      isalnu.mac


        Usage

                isalnum(c);
                int             c;

        Description

                Return  non-zero  if  c  is an alphanumeric character, 0
                otherwise.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-137
        isalpha Test for alphabetic argument


        5.109  Test for alphabetic argument                ____ ___ __________ ________



                                   ***********
                                   * isalpha *
                                   ***********



        File name:      isalph.mac


        Usage

                isalpha(c);
                int             c;

        Description

                Return  non-zero  if  c  is  an  alphabetic character, 0
                otherwise.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-138
        isascii Test for 7-bit Ascii character


        5.110  Test for 7-bit Ascii character                ____ ___ _____ _____ _________



                                   ***********
                                   * isascii *
                                   ***********



        File name:      isasci.mac


        Usage

                isascii(c);
                int             c;

        Description

                Return  non-zero  if  c  is  a  7-bit Ascii character, 0
                otherwise.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-139
        isatty  Test if terminal file


        5.111  Test if terminal file                ____ __ ________ ____



                                   **********
                                   * isatty *
                                   **********



        File name:      isatty.mac


        Usage

                isatty(channel_number)
                int             channel_number;

        Description

                Return  1  if  the  file  open  on  this  channel  is  a
                terminal-type device.  In general, this means the user's
                command terminal.  

                Note  that the argument is a file descriptor, not a FILE
                *  pointer.   File  descriptors  are  used  on  Unix  to
                identify  the  channel  on  which  the file is open.  As
                Decus C does not support file descriptor I/O processing,
                the logical unit number assigned to a file by fopen() is
                used instead.  Use isatty() as follows:  

                        if (isatty(fileno(fd))) ...

        Bugs

                Note  that  Decus  C  channel numbers are not related to
                Unix file descriptors.  Specifically, 

                        isatty(0)

                does not necessarily check stdin.  Use 

                        isatty(fileno(stdin))

                instead.  


[[        C Compiler and Library]]                                    Page 5-140
        iscntrl Test for control character argument ;02


        5.112  Test for control character argument              ;02                ____ ___ _______ _________ ________              ___



                                   ***********
                                   * iscntrl *
                                   ***********



        File name:      isctrl.mac


        Usage

                iscntrl(c);
                int             c;

        Description

                Return non-zero if C is a control character.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-141
        isdigit Return TRUE if digit argument


        5.113  Return TRUE if digit argument                ______ ____ __ _____ ________



                                   ***********
                                   * isdigit *
                                   ***********



        File name:      isdigi.mac


        Usage

                isdigit(c);
                int             c;

        Description

                Return 1 if c is an Ascii digit, 0 otherwise.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-142
        isgraph Test for graphic alphabetic argument


        5.114  Test for graphic alphabetic argument                ____ ___ _______ __________ ________



                                   ***********
                                   * isgraph *
                                   ***********



        File name:      isgrap.mac


        Usage

                isgraph(c);
                int             c;

        Description

                Return   non-zero   if  c  is  a  graphic  character,  0
                otherwise.  

                Graphics   characters   include   letters,  digits,  and
                punctuation.  Space, tab, etc.  are not graphics.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-143
        islower Test for lower-case alphabetic argument


        5.115  Test for lower-case alphabetic argument                ____ ___ __________ __________ ________



                                   ***********
                                   * islower *
                                   ***********



        File name:      islowe.mac


        Usage

                islower(c);
                int             c;

        Description

                Return   non-zero   if  C  is  a  lower-case  alphabetic
                character, 0 otherwise.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-144
        isprint Return non-zero if printable argument


        5.116  Return non-zero if printable argument                ______ ________ __ _________ ________



                                   ***********
                                   * isprint *
                                   ***********



        File name:      isprin.mac


        Usage

                isprint(c);
                int             c;

        Description

                Return  non-zero  if  c  is  a  printable  character,  0
                otherwise.  

                Printable    characters    include    letters,   digits,
                punctuation, and the  space  character.   Tab,  newline,
                etc.  are not included.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-145
        ispunct Return TRUE if punctuation argument


        5.117  Return TRUE if punctuation argument                ______ ____ __ ___________ ________



                                   ***********
                                   * ispunct *
                                   ***********



        File name:      ispunc.mac


        Usage

                ispunct(c);
                int             c;

        Description

                Return   non-zero  if  c  is  an  Ascii  punctuation,  0
                otherwise.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-146
        isspace Return non-zero if the character is "whitespace"


        5.118  Return non-zero if the character is "whitespace"                ______ ________ __ ___ _________ __ ____________



                                   ***********
                                   * isspace *
                                   ***********



        File name:      isspac.mac


        Usage

                isspace(c);
                int             c;

        Description

                Return  non-zero  if c is a whitespace character.  These
                consist  of  space,   backspace,   newline,   tab,   and
                form-feed.  The carriage return ('\r') is also included. 

        Bugs 


[[        C Compiler and Library]]                                    Page 5-147
        isupper Return TRUE if Upper-case alphabetic argument


        5.119  Return TRUE if Upper-case alphabetic argument                ______ ____ __ __________ __________ ________



                                   ***********
                                   * isupper *
                                   ***********



        File name:      isuppe.mac


        Usage

                isupper(c);
                int             c;

        Description

                Return  1  if c is an Upper-case alphabetic character, 0
                otherwise.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-148
        isxdigit        Return non-zero if hexadecimal digit


        5.120  Return non-zero if hexadecimal digit                ______ ________ __ ___________ _____



                                  ************
                                  * isxdigit *
                                  ************



        File name:      isxdig.mac


        Usage

                isxdigit(c);
                int             c;

        Description

                Return  non-zero if C is a valid hexadecimal digit (0-9,
                A-F, a-f).  

        Bugs 

                This routine is not present in other C libraries.  

[[        C Compiler and Library]]                                    Page 5-149
        itoa    Integer to Ascii


        5.121  Integer to Ascii                _______ __ _____



                                    ********
                                    * itoa *
                                    ********



        File name:      itoa.mac


        Usage

                char *
                itoa(value, string)
                int             value;
                char            *string;

        Description

                itoa  converts  the  value to a (signed) decimal string.
                The string is null-trailed.  itoa returns a  pointer  to
                the trailing null.  

                Note  that the result can be computed (more flexibly) by
                executing sprintf(buffer, "%d", value);  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-150
        itoa8   Convert integer to octal Ascii


        5.122  Convert integer to octal Ascii                _______ _______ __ _____ _____



                                    *********
                                    * itoa8 *
                                    *********



        File name:      itoa8.mac


        Usage

                char *
                itoa8(value, buffer);
                int             value;
                char            *buffer;

        Description:

                The  value  is  converted  to  octal  and  stored in the
                buffer.  A pointer to the trailing null is returned.  

                Note  that the result can be computed (more flexibly) by
                executing sprintf(buffer, "%o", value);  

        Bugs:  

                This  routine  does not generate leading zeros.  If they
                are needed, use:  

                        sprintf(buffer, "%06o", value);


[[        C Compiler and Library]]                                    Page 5-151
        itoax   Convert an integer to hexidecimal Ascii


        5.123  Convert an integer to hexidecimal Ascii                _______ __ _______ __ ___________ _____



                                    *********
                                    * itoax *
                                    *********



        File name:      itoax.mac


        Usage

                char *
                itoax(value, buffer);
                int             value;
                char            *buffer;

        Description:

                Convert the integer to hexidecimal ascii.  The string is
                null-trailed.   Values  from  10  to  15  (decimal)  are
                represented by "A" to "F".  Itoax() returns a pointer to
                the trailing null.  

                Note  that the result can be computed (more flexibly) by
                executing sprintf(buffer, "%x", value);  

        Bugs:  


[[        C Compiler and Library]]                                    Page 5-152
        kbin    Single Character Terminal Input


        5.124  Single Character Terminal Input                ______ _________ ________ _____



                                    ********
                                    * kbin *
                                    ********



        File name:      kbin.mac


        Usage

                int
                kbin();

        Description

                Read one character from the console terminal.  The input
                character is not echoed nor does the program delay until
                an entire line has been entered.  

                Note the following:  

                This   routine  is  very  inefficient,  as  it  requests
                operating-system service for every character entered.  

                Typing  Control/C  (or  Control/Y on VMS) will cause the
                program to exit immediately (as if  the  main()  routine
                exited), closing all files.  

                On  RT-11  (native  and  emulated), the operating system
                expands  <return>  to  a  carriage  return   line   feed
                sequence.   This  will  be  stripped  by  kbin() to just
                <return> ('\r' in C).  Thus, if the user  program  reads
                '\n', a <line-feed> was typed.  Note that this is unlike
                the general C library.  

        Bugs 

                On  RSX,  this  routine  requires  the  command terminal
                having been assigned as logical unit number 1.  

                In  general,  the  input  character  will  not have been
                echoed.  On RSTS/E and native RT11, the operating system
                may  already  have  echoed the character if you type the
                character before the read request has been made.  

[[        C Compiler and Library]]                                    Page 5-153
        kbinr   Terminal Input Without Wait


        5.125  Terminal Input Without Wait                ________ _____ _______ ____



                                    *********
                                    * kbinr *
                                    *********



        File name:      kbinr.mac


        Usage

                int
                kbinr();

        Description

                If  a  character has been typed on the console terminal,
                return it (without echoing or waiting).  If no character
                is available, kbin() returns -1 (EOF).  

                Note the following:  

                This   routine  is  very  inefficient,  as  it  requests
                operating-system service for every character entered.  

                Typing  Control/C  (or  Control/Y on VMS) will cause the
                program to exit immediately.  

                On  RT-11,  the  operating  system expands <return> to a
                carriage  return  line  feed  sequence.   This  will  be
                stripped  by kbin() to just <return> ('\r' in C).  Thus,
                if the user program reads '\n', a <line-feed> was typed.
                Note that this is unlike the general C library.  

        Bugs 

                On  RSX-11M,  this  routine depends on the fact that the
                console terminal was assigned to LUN 1.  

                On  RSX-11M  and VMS emulation mode, the typed character
                will not be echoed.  On RSTS/E and RT11  modes,  it  may
                have  already been echoed by the operating system if the
                terminal user typed before the program requests input.  


[[        C Compiler and Library]]                                    Page 5-154
        localtime       Build time of day buffer


        5.126  Build time of day buffer                _____ ____ __ ___ ______



                                  *************
                                  * localtime *
                                  *************



        File name:      localt.mac


        Usage

                #include <time.h>       /* Define tm structure  */

                struct tm *
                localtime(tvec);
                long            *tvec;  /* Time value pointer   */

                struct tm {
                  int   tm_sec;         /* Seconds              */
                  int   tm_min;         /* Minutes              */
                  int   tm_hour;        /* Hours                */
                  int   tm_mday;        /* Day of month         */
                  int   tm_mon;         /* Month 0 .. 11        */
                  int   tm_year;        /* Year - 1970          */
                  int   tm_wday;        /* Weekday, Sunday == 0 */
                  int   tm_yday;        /* Days since Jan 1     */
                  int   tm_isdst;       /* Daylight Saving if 1 */
                };

        Description

                localtime()  converts  a  Unix time value to a vector of
                values.  

        Bugs 

                Decus  C  doesn't  correct  for  time  zone  or daylight
                savings time.  

                Leap  year  isn't done correctly.  The routine will fail
                after Feb 28, 2100.  

                Following  Unix precedent, localt returns a pointer to a
                static buffer.  


[[        C Compiler and Library]]                                    Page 5-155
        malloc  Allocate and free memory


        5.127  Allocate and free memory                ________ ___ ____ ______



                                   **********
                                   * malloc *
                                   **********



        File name:      malloc.mac


        Usage

                char *
                malloc(size);           /* NULL if no space     */
                unsigned        size;   /* Number of bytes      */

                mfree(p);
                free(p);
                char            *p;     /* Was allocated        */

          Internal

                extern char *$$alhd;    /* Allocated block list */

                mov     size,r0         ; Internal call
                call    $$aloc          ; to malloc()

                Return: r0 -> space (or 0), other registers preserved

                mov     pointer,r0      ; Internal call
                call    $$free          ; to free()

                Return: r0 random, other registers preserved

        Description

                malloc()   allocates  the  indicated  number  of  bytes,
                returning a pointer to the  first.   If  the  allocation
                request  cannot  be satisfied, malloc returns NULL.  The
                program image is expanded as needed.  

                free()  and  mfree()  return  a  buffer  to  free space.
                Nothing is returned.  

                See also the description of realloc() and sbrk().  

        Internal 

                All  free  memory is allocated in linked lists which are
                stored in  monotonically  linked,  noncontiguous  areas.
                Each block has is preceeded by a one word header:  

[[        C Compiler and Library]]                                    Page 5-156
        malloc  Allocate and free memory



                        pointer to next block + "busy bit"

                The  pointer  is  to the next following block.  The last
                block points to the first.  The "busy bit" will  be  set
                if  the  data  in the block is in use.  $$alhd points to
                the first such block.  

                Note that a block need not contain any data.  Free space
                is coalesced during the allocation search.  

        Diagnostics 

                The  program  may  abort  if  free()  is passed a random
                pointer or if the program  writes  outside  of  an  area
                reserved  by malloc().  Note that only certain cases are
                trapped by this test and that free will  accept  invalid
                addresses,  which  will  cause mysterious failures.  The
                isalloc() function may be used to test whether  a  block
                of memory has been allocated by malloc().  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-157
        maxmin  Maximum and Minimum Routines


        5.128  Maximum and Minimum Routines                _______ ___ _______ ________



                                   **********
                                   * maxmin *
                                   **********



        File name:      maxmin.mac


        Usage

                max(a,b)
                int             a;
                int             b;

                min(a,b)
                int             a;
                int             b;

                unsigned
                maxu(a,b)
                unsigned        a;
                unsigned        b;

                unsigned
                minu(a,b)
                unsigned        a;
                unsigned        b;

        Description

                max()  and  min()  return, respectively, the maximum and
                minimum of their two  arguments,  considered  as  signed
                integers.   maxu()  and minu() are the same but consider
                their arguments to be unsigned.  

                Note:  If you are interested in getting the fastest code
                possible and have some knowledge of the  relative  sizes
                of  a  and  b,  arrange  for  a to be chosen most often.
                (It's unlikely  the  difference  will  be  noticable  in
                virtually all cases.) 

        Bugs 


[[        C Compiler and Library]]                                    Page 5-158
        memdmp  Dump memory or registers


        5.129  Dump memory or registers                ____ ______ __ _________



                                   **********
                                   * memdmp *
                                   **********



        File name:      memdmp.mac


        Usage

                memdmp(start, end);     /* Memory dump routine  */
                char            *start; /* First to dump        */
                char            *end;   /* Last to dump         */

                regdmp();               /* Register dump        */

          Internal

                call    regdmp          ;Register dump

                mov     #end,-(sp)      ;Last address   (or first)
                mov     #start,-(sp)    ;First address  (or last)
                call    memdmp          ;Dump memory

                mov     #start,r0       ;First address  (or first)
                mov     #end,r1         ;Last address   (or last)
                call    $$dump          ;Dump memory

                mov     value,r0        ;What to convert
                mov     #buffer,r1      ;Where it goes
                call    $$toct          ;Convert it

                Return:
                        r0      unchanged
                        r1      -> first free byte in buffer
                        r2-r5   unchanged

        Description

                Dump   registers   and/or  memory.   All  registers  are
                preserved.  

                If memdmp is called with a zero argument, the stack will
                be dumped.  

                Memdmp  and regdmp are independent of the C I/O library.
                However, on RSX, they assume that the  console  terminal
                has been assigned as LUN 1.  


[[        C Compiler and Library]]                                    Page 5-159
        memdmp  Dump memory or registers


        Bugs 

                Condition codes are not preserved.  


[[        C Compiler and Library]]                                    Page 5-160
        msg     Print a message on the command terminal


        5.130  Print a message on the command terminal                _____ _ _______ __ ___ _______ ________



                                     *******
                                     * msg *
                                     *******



        File name:      msg.mac


        Usage

                msg(text)
                char            *text;

          Internal

                mov     #text,r0
                call    $$msg

        Description

                Print  a  message on the console terminal.  This routine
                does  not  use  the  standard  library.   Return:    all
                registers are preserved.  

        Bugs 

                On  RSX,  this  routine  requires  the  command terminal
                having been assigned as logical unit number 1.  


[[        C Compiler and Library]]                                    Page 5-161
        msize   Get Size of a Memory Block


        5.131  Get Size of a Memory Block                ___ ____ __ _ ______ _____



                                    *********
                                    * msize *
                                    *********



        File name:      msize.mac


        Usage

                unsigned int
                msize(buff)
                char *buff;

        Description

                msize()  returns the size of a block of memory allocated
                by calloc(), malloc(), or realloc().  If buff  did  not,
                in  fact,  come  from one of these routines, the program
                will crash about 75% of  the  time;   the  other  25%  ,
                nonsense  will  be returned.  (This behavior is due to a
                simple-minded validation algorithm.)  However,  buff  ==
                NULL is valid and will return 0.  

                Note  that  the  value  returned is the amount of memory
                that malloc() (or whoever) actually allocated, which may
                not  be  exactly  the  same  as  the  program asked for.
                (Currently, all allocations are rounded up  to  an  even
                number of bytes.) 

        Bugs 

                Not portable.  

[[        C Compiler and Library]]                                    Page 5-162
        mul$l   Multiply long * long


        5.132  Multiply long * long                ________ ____ _ ____



                                    *********
                                    * mul$l *
                                    *********



        File name:      mull.mac


        Usage

                long
                mul$l(a, b);            /* long = long * long   */
                long            a;
                long            b;

                long
                mul$li(a, b);           /* Long = long * int    */
                long            a;
                int             b;

        Description

                Multiply  the long arguments.  This routine is called by
                the C compiler to compile long multiplies.  

                For  EIS,  given  two longs, A and B, in the word format
                Ah,As,Al and Bh,Bs,Bl where Ah is the high word, As  the
                sign  bit  of the low word, and Al the remaining 15 bits
                of the low order word.  Then 

                      A * B = Al * Bl  +  As * Bl * 2**15  +  Bs * Al *
                2**15
                                       +  Al * Bh * 2**16  +  Bl * Ah *
                2**16

                This derivation was provided by Cliff Geschke.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-163
        peek    Peek at a location in RSTS/E


        5.133  Peek at a location in RSTS/E                ____ __ _ ________ __ ______



                                    ********
                                    * peek *
                                    ********



        File name:      peek.mac


        Usage

                peek(location)
                int             *location;

        Description

                Peek to a location in the RSTS/E monitor.  

                The  job will be aborted with a BPT if not running under
                RSTS/E.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-164
        perror  Print Library Error Message


        5.134  Print Library Error Message                _____ _______ _____ _______



                                   **********
                                   * perror *
                                   **********



        File name:      perror.mac


        Usage

                perror(text)
                char            *text;

        Description

                An error message is written to stderr, using the current
                i/o library error (stored in $$ferr).  Text is prepended
                to the message.  

        Diagnostics 

        Bugs 


[[        C Compiler and Library]]                                    Page 5-165
        printf  Formatted print routine


        5.135  Formatted print routine                _________ _____ _______



                                   **********
                                   * printf *
                                   **********



        File name:      printf.mac


        Usage

                printf(format, arg1, ...)
                char            *format;

                fprintf(iov, format, arg1, ...)
                FILE            *iov;
                char            *format;

                char *
                sprintf(buffer, format, arg1, ...);
                char            *buffer;
                char            *format;

                $$prnt(format, argvec, iov)
                char            *format;
                int             *argvec[];
                FILE            *iov;

        Description

                printf()  converts,  formats,  and prints its arguments,
                under control of the first argument, writing output  via
                putchar().  fprintf() writes its output to the indicated
                file.  sprintf() writes  its  output  to  the  indicated
                string buffer.  $$prnt() is the internal print formatter
                which is called by printf, etc.  

                sprintf() returns a pointer to the EOS at the end of the
                output buffer.  This is not necessarily transportable.  

                The format argument is a character string which contains
                two types  of  objects:   plain  characters,  which  are
                simply  copied  to  the  output  stream,  and conversion
                specifications, each  of  which  causes  conversion  and
                printing of the next successive argument to printf.  

                Each  conversion  specification  is  introduced  by  the
                character %.  Following the %, there may be 

                 - an  optional  minus  sign  "-"  which  specifies left

[[        C Compiler and Library]]                                    Page 5-166
        printf  Formatted print routine


                   adjustment of the converted argument in the indicated
                   field.

                 - an optional digit string specifying field  width;  if
                   the  converted argument has fewer characters than the
                   field width, it will be blank-padded on the left  (or
                   right, if  the  left-adjustment  indicator  has  been
                   given) to make up the  field  width.   If  the  field
                   width  is  specified as '*' or '?', the next argument
                   is used.  (Note: '?' is  obsolete.)  If the  width is
                   specified  with a leading  zero,  zeros are  used for
                   padding instead of blanks.  This zero  does NOT imply
                   an octal field width.  For example, assume the  value
                   123 is to be printed:
                        %d      "123"
                        %5d     "  123"
                        %-5d    "123  "
                        %05d    "00123"

                 - an  optional  period "." which serves to separate the
                   field width from the next digit string;

                 - an optional digit string (precision) which  specifies
                   the number of digits  to  appear  after  the  decimal
                   point for e- and f-conversion, or the maximum  number
                   of  characters  to be printed from a string.   If the
                   precision is  specified  as  '*'  or  '?',  the  next
                   argument is used.

                 - a character which indicates the  type  of  conversion
                   to be applied.

                The conversion characters and their meanings are 

                 d      Signed-decimal
                 u      Unsigned-decimal
                 o      Octal
                 X      Hexadecimal, 10-15 are represented by A-F
                 x      Hexadecimal, 10-15 are represented by a-f

                        The  integer  argument  is converted to decimal,
                        octal, or hexadecimal   notation   respectively.
                        Any   of   the   conversion  characters  may  be
                        preceeded  by  'l'  to  signal  "long"   integer
                        argument.   Note  that the Unix usage of capital
                        letters  to  represent  long  arguments  is  not
                        supported.

                                             Note

                            In order to  eliminate  the  very  large
                            floating  point conversion routines from
                            most programs, a program which  requires
                            floating  point  conversion must request

[[        C Compiler and Library]]                                    Page 5-167
        printf  Formatted print routine


                            the  double  to ascii conversion routine
                            explicitly.    The  following  sequences
                            show how this is done:

                        RSX: TKB task=source,LB:DTOA,LB:C/LB
                       RT11: LINK source,C:DTOA,C:SUPORT,C:CLIB/BOT:2000

                            If this is not done, any use of  the  %f
                            %e, or %g conversions will result in  an
                            error  message.   On RSTS/E, the library
                            build procedure creates  RTDTOA.OBJ  and
                            RXDTOA.OBJ in the library account.

                            ** Floating point support has not yet **
                            ** been fully implemented.  The float **
                            ** or  double  value must be the last **
                            ** or only argument to printf.   Only **
                            ** single-precision   conversion   is **
                            ** presently available.               **

                 f      The  argument  is  converted to decimal notation
                        in the style "[-]ddd.dd" where the number of d's
                        after  the  decimal  point  equals the precision
                        specification for the argument.  If precision is
                        missing, 6 digits are given; if explicitly 0, no
                        digits and no decimal point  are  printed.   The
                        argument  should  be  float or double.  "%lf" or
                        "%F" must be used to signal "long (i.e.  double)
                        argument."  This is a restriction of Decus C.

                 e      The float or double argument is converted in the
                        style "[-]d.ddde+-dd" where there is  one  digit
                        before the decimal point and the number after is
                        equal  to  the  precision   specified   for  the
                        argument;  if the precision is missing, 6 digits
                        are produced.  "%le" or "%E"  must  be  used  to
                        signal "long (i.e. double) argument."  This is a
                        restriction of Decus C.

                 g      Floating point:  "%f" format if  suitable,  else
                        "%e"  format.   "%lg"  or  "%G"  must be used to
                        signal "long (i.e. double) argument."  This is a
                        restriction of Decus C.

                 c      The argument character is printed.   (Note  that
                        'lc' takes a long integer argument.)

                 r      Remote format.  The next  printf()  argument  is
                        the format.  Note that this is not a subroutine.
                        The current format is not processed further. For
                        example:

                                bug(args)
                                {

[[        C Compiler and Library]]                                    Page 5-168
        printf  Formatted print routine


                                        error("Error at %r", &args);
                                }

                        This routine might be called as follows:

                                bug("Error %d at %s\n", val, name);

                        %r is not transportable to  all  implementations
                        of  the  standard  library.  It does not word on
                        Vax-11 C, for example.  $$prnt may  be  used
                        as shown below for similar functionality.

                 s      The  argument is taken to be a string (character
                        pointer) and  characters  from  the  string  are
                        printed  until  a  null  character  or until the
                        number of characters indicated by the  precision
                        specification  is   reached;   however   if  the
                        precision   specification  is  0  or missing all
                        characters up to null are printed.

                If  no  recognizable character appears after the %, that
                character is printed;  thus % may be printed by the  use
                of  the  string  %%.   In no case does a non-existant or
                small field width cause truncation of a field;   padding
                takes  place  only  if the specified field width exceeds
                the actual width.  Characters generated by printf()  are
                printed by calling putchar().  

                $$prnt()  is  the internal print formatter called by all
                "top-level"  print  functions.    It   is   functionally
                identical  to  the  Unix  and Vax-11 C _doprnt() library
                routine.  Unfortunately, the leading '_' conflicts  with
                RSX-11M   file  services  library  routine  conventions,
                requiring the use of the Decus C unique "$$" prefix.  If
                your   programs  wish  to  call  $$prnt,  a  potentially
                transportable procedure would be:  

                    #ifdef decus
                        $$prnt(format, args, iov);
                    #else
                        _doprnt(format, args, iov);
                    #endif

                You  should  assume,  however,  that  _doprnt()  is  not
                necessarily  present  on  all  implementations  of   the
                "standard library." 

        Bugs 

                e,  f,  and  g conversion only work for single-precision
                floating point.  Use of "%lf" etc.  is not transportable
                and  may  change.   It  may also cause problems in the C
                compiler (as the standard  says  that  subroutine  calls
                take double (not short floating) arguments.  

[[        C Compiler and Library]]                                    Page 5-169
        printf  Formatted print routine




[[        C Compiler and Library]]                                    Page 5-170
        profile Print profile data


        5.136  Print profile data                _____ _______ ____



                                   ***********
                                   * profile *
                                   ***********



        File name:      profil.mac


        Usage

                $$prof();

                extern  int     $$prnl;

                extern  char    *$$pfil;


        Description

                $$prof  is  called  by  the  run-time  library  when the
                program exits if any functions have been  executed  that
                were compiled with the profile option.  

                A profile file is written to file "profil.out".  This is
                defined by a global symbol $$pfil.  By setting $$prnl to
                NULL, the profile file is supressed.  

                By changing the value of $$prnl, the program can control
                the number of profile entries written on each line.  The
                default  value  writes  4  entries  per  line.  Changing
                $$prnl to N writes N entries on  each  line,  simplifing
                post-processing (sorting) of the data.  For example:  

                        $$prnl = 0;

                writes each entry on a separate line.  

                The  following  example  shows how to control the output
                file name:  

                        extern char *$$pfil;
                        ...
                        $$pfil = "ti:"; /* Output to ti:        */
                        $$pfil = NULL;  /* No profile output    */


                Data  is  written using the format string "%8s %6u".  If
                more than one entry is written  to  a  line,  succeeding
                entries will be preceeded by one space.  

[[        C Compiler and Library]]                                    Page 5-171
        profile Print profile data



                Note  that,  by writing the data one entry per line, the
                profile output may easily be sorted either  by  function
                name or by frequency count.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-172
        putc    Output one character to a file


        5.137  Output one character to a file                ______ ___ _________ __ _ ____



                                    ********
                                    * putc *
                                    ********



        File name:      putcha.mac


        Usage


                putchar(c);
                char            c;

                putc(c, iop);
                char            c;
                FILE            *iop;

        Description

                Putchar()  writes  one  character to the standard output
                file.  Putc() writes one character to the  named  output
                file.  

                Normally, the character is returned.  EOF is returned on
                errors.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-173
        puts    Output a string to a file


        5.138  Output a string to a file                ______ _ ______ __ _ ____



                                    ********
                                    * puts *
                                    ********



        File name:      puts.mac


        Usage

                puts(s);
                char            *s;

                fputs(s, iop);
                char            *s;
                FILE            *iop;

                fputss(s, iop);
                char            *s;
                FILE            *iop;

        Description

                puts()  writes  a  string  to  the  standard output.  It
                appends a newline after the string.  

                fputs()  writes  a  string  to  the  indicated file.  No
                newline is appended.  

                fputss()  writes  a  string  to  the  indicated file.  A
                newline is appended.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-174
        putw    Output a binary integer to a file


        5.139  Output a binary integer to a file                ______ _ ______ _______ __ _ ____



                                    ********
                                    * putw *
                                    ********



        File name:      putw.mac


        Usage

                putw(word, iop);
                int             word;
                FILE            *iop;

        Description

                putw()  writes  one  word  to  the  indicated  file.  It
                returns EOF on error, 0 on success 

        Bugs 


[[        C Compiler and Library]]                                    Page 5-175
        qset    Add memory to the RT11 queue area


        5.140  Add memory to the RT11 queue area                ___ ______ __ ___ ____ _____ ____



                                    ********
                                    * qset *
                                    ********



        File name:      qset.mac


        Usage

                qset(number)
                int     number; /* How many elements            */

        Description

                Allocate  sufficient  memory for the requested number of
                queue  elements.   If  sufficient   memory   cannot   be
                allocated, do nothing.  

        Bugs 

                This routine is ignored on RSX.  


[[        C Compiler and Library]]                                    Page 5-176
        r50toa  Convert Radix-50 to Ascii


        5.141  Convert Radix-50 to Ascii                _______ ________ __ _____



                                   **********
                                   * r50toa *
                                   **********



        File name:      r50toa.mac


        Usage

                r50toa(buff, r5vec, r5cnt);
                char            *buff;  /* Output text buffer   */
                int             *r5vec; /* Input rad50 buffer   */
                int             r5cnt;  /* How many rad50 words */

        Description:

                Convert  r5cnt  words  of  radix  50 data to Ascii.  All
                letters will be in upper-case.  The output  buffer  will
                not be null-trailed, nor will blank fields be supressed. 

        Bugs 


[[        C Compiler and Library]]                                    Page 5-177
        rand    Random number generator


        5.142  Random number generator                ______ ______ _________



                                    ********
                                    * rand *
                                    ********



        File name:      rand.mac


        Usage

                long
                rand()

                extern long     seed;   /* Random number seed   */

        Description

                Generate a pseudorandom number.  

                The algorithm is:  

                    seed = (69069 * seed + 1);
                    return (rand & 0X8FFFFFFF);

                The algorithm is based on the mth$random function in the
                VMS common run-time library.  

                Note  that the algorithm is prone to nonrandom sequences
                when considering the next pseudorandom number.  

        Bugs 



[[        C Compiler and Library]]                                    Page 5-178
        realloc Reallocate memory


        5.143  Reallocate memory                __________ ______



                                   ***********
                                   * realloc *
                                   ***********



        File name:      reallo.mac


        Usage

                char *
                realloc(buff, size);
                char            *buff;  /* Buffer from malloc() */
                unsigned        size;   /* New size for buff    */

        Description

                Realloc()  changes  the  size of the block pointed to by
                buff, returning a pointer to the (possibly moved) block.
                The  contents  will be unchanged up to the lesser of the
                new and old sizes.  

                Realloc()  also  works  if  buff points to a block freed
                since the last call of malloc(), realloc(), or calloc();
                thus  sequences  of  free(), malloc(), and realloc() can
                exploit the search strategy of malloc()  to  do  storage
                compaction.  

                See  also  the  description  of  malloc(),  calloc() and
                sbreak().  

                The   following   program  segment  illustrates  use  of
                realloc() to expand and compact storage.  

                        #ifndef vms
                        static char *compact_work;
                        #endif

                        main() {
                                /*
                                 * Initialize work element
                                 * for compact()
                                 */
                        #ifndef vms
                                compact_work = malloc(1);
                        #endif
                                ...
                        }


[[        C Compiler and Library]]                                    Page 5-179
        realloc Reallocate memory


                        char *
                        compact(old_ptr, new_size)
                        char    *old_ptr;
                        int     new_size;
                        /*
                         * Reallocate the area allocated to old_ptr,
                         * originally allocated by a call to malloc(),
                         * so that it will contain new_size bytes (which
                         * may be greater or less than the current
                size).
                         * Return a pointer to the new area.
                         * Note:  error handling is not shown.
                         */
                        {
                                extern char *realloc();

                                free(old_ptr);
                        #ifndef vms
                                free(compact_work);
                                compact_work = malloc(1);
                        #endif
                                return(realloc(old_ptr, new_size));
                        }

                compact_work must not be used on the native vax compiler
                (Vax-11 C) as  the  internal  free  memory  buffers  are
                organized in a different and incompatible manner.  

        Diagnostics 

                The  program  will abort if buff is not the address of a
                buffer allocated by malloc() or calloc().  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-180
        rewind  Rewind a file for re-reading


        5.144  Rewind a file for re-reading                ______ _ ____ ___ __________



                                   **********
                                   * rewind *
                                   **********



        File name:      rewind.mac


        Usage

                rewind(iop);
                FILE            *iop;

        Description

                Rewind  the  indicated file.  Return -1 if failure, 0 if
                ok.  

                On RT11, if the file was opened for output, it is closed
                and reopened for input.  

        Diagnostics 

                RT11 exits fatally if the file name won't parse.  As the
                filename was stored by fopen(), this probably means that
                the user program has stored randomly in memory.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-181
        rindex  Find Last Instance of a Character in a String


        5.145  Find Last Instance of a Character in a String                ____ ____ ________ __ _ _________ __ _ ______



                                   **********
                                   * rindex *
                                   **********



        File name:      rindex.mac


        Usage

                char *
                rindex(stng, chr)
                char            *stng;  /* String to search in  */
                char            chr;    /* Byte to search for   */

        Description

                If chr is in stng, return a pointer to the last instance
                it.  If not, return NULL.  

        Bugs 

                Obsolete, use strrchr() instead.  


[[        C Compiler and Library]]                                    Page 5-182
        rstsys  Execute a RSTS EMT


        5.146  Execute a RSTS EMT                _______ _ ____ ___



                                   **********
                                   * rstsys *
                                   **********



        File name:      rstsys.mac


        Usage

                int
                rstsys(emt)

        Description

                Execute a rsts emt, returning the error code.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-183
        rtemt   Execute a RT11 EMT


        5.147  Execute a RT11 EMT                _______ _ ____ ___



                                    *********
                                    * rtemt *
                                    *********



        File name:      rtemt.mac


        Usage

                int
                rtemt(emt, r0value)

        Description

                Execute a rt11 emt after loading r0.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-184
        salloc  Allocate local memory


        5.148  Allocate local memory                ________ _____ ______



                                   **********
                                   * salloc *
                                   **********



        File name:      salloc.mac


        Usage

                char *
                salloc(n);              /*   NULL if no space   */

        Description

                Allocate  the  requested number of bytes on the run-time
                stack, returning a pointer to the first byte  allocated.
                The  storage  will  be  reclaimed automatically when the
                function that called salloc() exits.  

                Note  that  storage  so  allocated  cannot be explicitly
                freed.  

                salloc()  returns NULL if allocating the requested space
                would cause the run-time stack to go below 1000 octal.  

                Note:   it  is  essential that salloc() be called with a
                "clean stack".  I.e, the program must not execute 

                        subr(salloc(10), 20);

                Instead, it should execute 

                        temp = salloc(10);
                        subr(temp, 20);

        Diagnostics

        Bugs


[[        C Compiler and Library]]                                    Page 5-185
        sbrk    Allocate memory from operating system


        5.149  Allocate memory from operating system                ________ ______ ____ _________ ______



                                    ********
                                    * sbrk *
                                    ********



        File name:      sbrk.mac


        Usage

                char *
                sbrk(amount)
                int             amount;

        Description

                sbrk() allocates the indicated amount of memory from the
                operating system.  The allocation is permanent.  

        Diagnostics 

                NULL   is  returned  if  the  memory  requested  is  not
                available.  There is no "shortened" return.  

        Bugs 

        Internal 

                Sbrk() does not modify its argument.  



[[        C Compiler and Library]]                                    Page 5-186
        scanf   Formatted input conversion


        5.150  Formatted input conversion                _________ _____ __________



                                    *********
                                    * scanf *
                                    *********



        File name:      scanf.mac


        Usage

                scanf(fmt, pointer(s))
                char            *fmt;   /* Format string        */

                fscanf(fd, fmt, pointer(s))
                FILE            *fd;    /* Input file pointer   */
                char            *fmt;   /* Format string        */

                sscanf(buf, fmt, pointer(s))
                char            *buf;   /* Input text buffer    */
                char            *fmt;   /* Format string        */

                $$scan(fmt, argp, iov)
                char            *fmt;   /* Format string        */
                int             *ptr[]; /* Pointer vector       */
                FILE            *iov;   /* Input file des.      */

        Description

                Using the format string, these functions parse the input
                file (or given text file), storing the  results  in  the
                pointer  arguments.   The  three  user-callable routines
                differ as follows:  

                        scanf   Reads from the standard input file.

                        fscanf  Reads from the indicated file.

                        sscanf  Reads from the text buffer.

                $$scan()  is  an internal routine called by the above to
                actually parse  the  input  text.   It  is  functionally
                identical  to  the  Unix and Vax-11 C _doscan() routine.
                Unfortunately, the leading '_' conflicts with  RSX  file
                control service routine naming conventions.  

                The  format  string  may  contain  control characters to
                direct the conversion of the input textual data:  

                  ' '   Blanks, tabs, or newlines are ignored in  format

[[        C Compiler and Library]]                                    Page 5-187
        scanf   Formatted input conversion


                        strings.  To match whitespace, use "%[ \t\n]".

                   x    An  ordinary  character  (not  %) must match the
                        next input character.

                   %    Conversion specifications consist of a  '%',  an
                        optional   '*'  (to   supress   assignment),  an
                        optional  maximum  numeric  field  width,  and a
                        conversion specifier.

                Unless  value assignment was supressed by the '*' format
                modifier, the next field is converted and stored in  the
                variable  pointed  to by the corresponding argument.  An
                input  field  is  defined  as  a  string  of   non-space
                characters,   extending   to   the  first  inappropriate
                character  or  until  the  field  width  (if  given)  is
                exhausted.  

                The following conversion characters are specified:  

                  %     A single  '%'  is  expected  in  the  input,  no
                        assignment is done.

                  d     An integer  of  the  specified  class  (decimal,
                  o     octal,  or  hexadecimal)   is   expected.    The
                  x     corresponding  argument  should  be  an  integer
                        pointer.   If   the  format specifer is given in
                        upper-case, or preceeded by 'l', a long  integer
                        will be stored.  For example, "%ld" is identical
                        to "%D".   Leading  whitespace  will be ignored.
                        A null field is not converted.  Scanf()  returns
                        a  count  of the number of fields converted, but
                        does not indicate which fields were ignored.

                  s     A character string is expected.  The input field
                        will be terminated by a space, tab, or  newline.
                        The corresponding argument  should  point  to  a
                        buffer large enough to contain the  text  and  a
                        terminating  NULL.   Leading  whitespace will be
                        ignored.

                  c     A single character is read. Leading white  space
                        is not supressed  --  to read the next non-blank
                        character, use "%1s".  If a field width is given
                        the  corresponding  argument  is  a pointer to a
                        vector of characters and the indicated number of
                        characters are read.

                  e     A floating-point number is converted and  stored
                  f     appropriately.    If  the  format  indicator  is
                  g     capitalized, or  preceeded  by  'l',  a  double-
                        precision  floating-point number will be stored.
                        The floating-point format is the same as in  the
                        C language:   an  optionally  signed  string  of

[[        C Compiler and Library]]                                    Page 5-188
        scanf   Formatted input conversion


                        digits  possibly  containing  a  decimal  point,
                        followed by an  optional  exponent  field  which
                        consists  of  an  'E'  or  'e'  followed  by  an
                        optionally signed integer.

                 [ ]    A string not  to  be  delimited  by  white-space
                        characters.  Unless the first character is  '^',
                        the format constitutes an acceptance  list:  the
                        input field is all characters  until  the  first
                        character  which  is  not  in  the  set   within
                        brackets.   Note  that leading whitespace is not
                        ignored.

                        If the first character after the left bracket is
                        '^', the format defines a stop list:  the  input
                        field   is   all   characters  until  the  first
                        character specified within the bracketed string.

                        The corresponding argument points to a character
                        vector.  The result will be null-terminated.

                Scanf()  returns  the number of successfully matched and
                assigned input items.  If the end of input was  reached,
                EOF (-1) is returned.  For example:  

                        main()
                        {
                                register int    c;
                                int             i;
                                char            text[10];

                                c = scanf("%d%9s", &i, &text);
                                printf("i = %d, text = %s\n",
                                        i, text);
                        }

                If  the  input  line  is  "150 foobar", the program will
                print:  

                        i = 150, text = foobar

        Diagnostics

                Scanf()  returns  -1  if  an end of file (end of string)
                condition exists and no data was stored.  It returns  -2
                if   a   palpably  incorrect  format,  such  as  "%"  is
                encountered.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-189
        screen  Screen I/O Primitives


        5.151  Screen I/O Primitives                ______ ___ __________



                                   **********
                                   * screen *
                                   **********



        File name:      screen.mac


        Usage

                scdown()                /* Roll screen down     */

                scerln(line, column)    /* Erase to end of line */
                int             line;   /* Line number          */
                int             column; /* Column number        */

                scerpg(line, column)    /* Erase to end of page */
                int             line;   /* Line number          */
                int             column; /* Column number        */


                char *
                scget(buff, size, text)
                                        /* Prompt and read      */
                char            *buff;  /* Returned text        */
                int             size;   /* Buffer size          */
                char            *text;  /* Optional prompt      */


                int
                sclmargin(lmarg)        /* Set left margin      */
                int             lmarg;  /* New left margin      */


                scout(line, column, text)
                                        /* Write text to screen */
                int             line;   /* Line number          */
                int             column; /* Column number        */
                char            *text;  /* Text to write        */


                scput(oldbf)            /* Reset buffer mode    */
                char            *oldbf; /* Previous buffer      */


                int
                scset(newbf, size, old)
                                        /* Set buffer mode      */
                char            *newbf; /* New buffer           */

[[        C Compiler and Library]]                                    Page 5-190
        screen  Screen I/O Primitives


                char            size;   /* Size of new buffer   */
                char            **old;  /* Previous buffer save */


                int
                scsettype(type)         /* Force terminal type  */
                int             type;   /* Terminal type        */


                int
                sctype()                /* Return terminal type */


        Description

                Based on the "terminal independent screen procedures" in
                the VAX/VMS runtime library, these routines  provide  an
                efficient,  operating-system  independent,  interface to
                (DIGITAL) video terminals.   They  work  correctly  with
                VT52   and   VT100   (ANSI)  terminals  and  do  nothing
                disasterous if the terminal is not a video terminal.  

                Note  that  they  only  work  with  the  user's  console
                (stderr) terminal.  

                The following definitions should be noted:  

                        line    The line on  the  screen  to  which  the
                                cursor  is  to be moved.  The top of the
                                screen is line one.   If  line  is  less
                                than  or  equal to zero, the cursor does
                                not move.

                        column  The column to which the cursor is to  be
                                moved.  This value will be offset by the
                                left-margin value (if one is set).   The
                                default  left-hand margin is column one.
                                If column  (after  offsetting)  is  less
                                than  or  equal to zero, the cursor does
                                not move.

                        text    A null-terminated string to  be  output.
                                If  text  equals NULL, nothing is output
                                and internal buffers are flushed.

                The routines are designed to operate in a buffered mode,
                allowing the program  to  format  an  entire  screen  of
                information  and  present this data with one call to the
                monitor-level  I/O  service.   This   is   particularily
                efficient  on  multi-user  or  networked  systems.   The
                routines  scput()  and  scset()  establish  and  release
                buffer  mode.  Buffers can be chained together, allowing
                a subroutine to establish a buffer independently of  its
                callers.   Each  buffer  must be at least 12 bytes long.

[[        C Compiler and Library]]                                    Page 5-191
        screen  Screen I/O Primitives


                Longer buffers are more efficient.  

                Although  multiple  buffers can be established, only one
                is active at any particular time.  If a call to  scset()
                establishes  a  new buffer, the contents of the previous
                buffer are copied to the new  buffer  and  the  previous
                buffer  is set empty.  If scput() releases a buffer, its
                contents are copied to any higher-level buffer.  

                The  first  call  to any routine determines the terminal
                type.  Note that on native RT11, if the  screen  handler
                decides  that  the terminal may be a scope, it will send
                an "identify" request "<ESC>/Z" to determine whether  it
                is  a VT52 or VT100.  If the screen routine decides that
                the terminal is not a scope, cursor move operations  are
                ignored  and  text is output to "stderr".  If the screen
                handler decides that the terminal is a VT100, the "Enter
                ANSI mode" escape sequence will be sent to the terminal.
                Similarily, if the terminal is thought to be a VT52, the
                "Enter  VT52 emulation mode" sequence will be sent.  The
                screen handler will not  record  the  current  mode  for
                subsequent resetting.  

                Screen output will be to the "stderr" device (explicitly
                the console terminal).  Input will be from  the  "stdin"
                device.   If  a  local  buffer has been established, the
                screen handler calls operating system service  directly,
                bypassing  the  "standard" I/O library.  This means that
                output formatting should use sprintf() to format a  user
                buffer  which  is  subsequently  output  using  scout().
                Furthermore, the newline  '\n'  character  will  not  be
                expanded  to a "carriage return/line feed" sequence.  It
                is thus highly recommended that the user program perform
                all  formatting  by  passing  appropriate row and column
                values to scout().  

                The following routines are defined:  


                        scdown()

                The  cursor  is moved up one line on the screen.  If the
                cursor was already at the top line on  the  screen,  all
                lines  are moved down one line, the top line is replaced
                with a blank, and the data that was on the  bottom  line
                is lost.  (VMS Lib$Down_Scroll) 


                        scerln(line, column)

                Erase  the screen from the indicated (or current) cursor
                position  to  the  end  of  the  current   line.    (VMS
                Lib$Erase_Line) 


[[        C Compiler and Library]]                                    Page 5-192
        screen  Screen I/O Primitives



                        scerpg(line, column)

                Erase  the screen from the indicated (or current) cursor
                position to the end of the screen.  (VMS Lib$Erase_Page) 


                        scget(buff, size, text)

                Output  the  prompt  text,  if  given,  then  flush  any
                buffered text.  Read text input  by  the  terminal  user
                (from stdin) to the buffer.  Scget() returns NULL on end
                of file or error.  (Scget calls fgetss() to perform  the
                read.)  (VMS  Lib$Get_Screen)  Programs using scget() to
                read  from  the  keyboard  should  not  use  the   input
                redirection capabilities of the C library.  


                        sclmargin(lmarg)

                Define  a  new  left  margin  (if  lmarg is greater than
                zero).  Sclmargin() returns the old lmarg value.   After
                calling  sclmargin(),  an  output  request to column one
                will be written to column lmarg.  


                        scout(line, column, text)

                Move  the  cursor  to  the indicated line and column and
                output the text.  If line or column  are  less  than  or
                equal  to  zero,  the  cursor  is not moved.  If text is
                equal  to  NULL,  the  internal  buffers   are   flushed
                (possibly after cursor movement).  (VMS Lib$Put_Screen) 


                        scput(oldbf)

                Scput()   terminates  the  current  buffering  mode  and
                reverts  to  the  previous  mode  as  specified  in  the
                parameter.   If  oldbuf is NULL, buffering is terminated
                and the current buffer is flushed  to  the  screen.   If
                oldbuf  is  not  zero,  it is taken as the location of a
                previous buffer (established by calling scset()) and the
                current  buffer is copied into the previous buffer.  The
                previous   buffer   is   then   made   current.     (VMS
                Lib$Put_Buffer) 


                        scset(newbf, size, old)

                Scset()   establishes   a  new  buffer  for  the  screen
                routines.  Newbf is a  character  array  whose  size  is
                given  in  parameter  size  (Size  must  be  at least 12
                bytes.) Old is the address of a word which will  be  set

[[        C Compiler and Library]]                                    Page 5-193
        screen  Screen I/O Primitives


                to  the  previous  buffer  (if any).  This is used for a
                subsequent call  to  scput().   Scset  returns  zero  if
                correct,  returning  -1  if size was less than 12 bytes.
                (VMS Lib$Set_Buffer).  

                A  larger  buffer  will generally yield a more efficient
                program as the number of operating system requests  will
                be  minimized.   For  example,  for a typeout program, a
                buffer size of 800 bytes might well be used.  


                        scsettype(type)

                This  routine  sets  the  terminal  type, overriding the
                definition   supplied   by   the    operating    system.
                scsettype()  returns what it thought the type was (as if
                sctype were called).   The  type  must  be  one  of  the
                following values:  

                        0       Not a video terminal
                        65      VT52 or VT100 in VT52 mode
                        97      VT100 in ANSI mode

                If  type  has  some  other  value,  scsettype() does not
                change the type.  


                        sctype()

                This  routine  returns the terminal type.  The following
                types are defined:  

                        0       Not a video terminal
                        1       Unknown video terminal
                        1+64    VT52
                        1+96    VT100 type

                Note:   On  intitialization, a VT100 will be forced into
                VT52 or VT100 mode depending  on  the  determined  type.
                VT100-type terminals include newer terminals such as the
                VT125.  It is not clear whether the  algorithm  used  is
                correct  for  terminals  developed  since these routines
                were written.  

                Note the following normal use of scset() and scput() 

                        char    **oldbuf;
                        char    mybuf[100];

                        main()
                        {
                            /*
                             * Setup
                             */

[[        C Compiler and Library]]                                    Page 5-194
        screen  Screen I/O Primitives


                            scset(mybuf, sizeof mybuf, &oldbuf);
                            /*
                             * Usage
                             */
                            scout(1, 1, "Stuff");
                            /*
                             * Termination (force out last buffer)
                             */
                            scout(0, 0, NULL);
                            scput(oldbuf);
                        }


        Bugs

                These  routines  are  fairly inefficient if no buffer is
                supplied.  

                Determining the terminal type turns out to be a somewhat
                painful process  which  is  different  for  the  various
                operating systems:  

                On  native  RSX-11M  and VMS compatibility mode, the QIO
                "get multiple characteristics function" is executed.  If
                the   terminal  is  a  scope  and  can  generate  escape
                sequences, it is assumed to be a VT100, otherwise, if it
                is a scope, it is assumed to be a VT52.  

                On  all  RSTS/E  systems,  the  executive  "get terminal
                characteristics" request is executed, the  determination
                proceeding as above.  

                On native RT11 systems, a peek sequence described in the
                RT11  Software  Support  manual  is  used  to  determine
                whether  the terminal is a scope.  (This may not work on
                the XM monitor.) If so, an "<ESC>/Z" is sent to  request
                identification   and  various  tests  are  made  on  the
                returned text.  Note that,  if  the  terminal  does  not
                reply  to  the  inquiry,  the  program will hang.  These
                tests are valid for VT52 and VT100 terminals only.   You
                will  have  to  modify this routine if you have anything
                else (including a VT125).  

                On RSX-11M systems (even emulated), if a local buffer is
                established by calling  scset(),  output  will  be  done
                using the IO.WAL QIO function.  


                While  based  on  the  VMS  Run-time  library screen I/O
                primitives, there are a few differences that may  be  of
                interest:  

                The   VMS  library  standard  assumes  that  subroutines
                generally  return  a   status   code,   permit   missing

[[        C Compiler and Library]]                                    Page 5-195
        screen  Screen I/O Primitives


                parameters,  and  return  error codes on being presented
                with invalid arguments.  The routines described here  do
                nothing  when  arguments  are out of range.  Also, there
                are no optional arguments (optionality is  provided  for
                by  specifing  zero  or  NULL  argument  values).  Where
                appropriate,  arguments  have  been  ordered   "line_no,
                col_no, other".  

                A  more  significant  difference is that the VMS library
                writes to the standard output  device  (SYS$OUTPUT:   or
                TT:)  while  these routines write to the user's terminal
                (SYS$ERROR or CO:).  scget()  reads  from  the  standard
                input.  


[[        C Compiler and Library]]                                    Page 5-196
        setcc   Trap Control/C (RSTS/E RT11 mode only)


        5.152  Trap Control/C (RSTS/E RT11 mode only)                ____ _________ _______ ____ ____ _____



                                    *********
                                    * setcc *
                                    *********



        File name:      setcc.mac


        Usage

                setcc(function);
                extern int function();

        Description

                The  function  is  defined  as  a  CTRL/C  trap routine.
                Executing setcc(0) disables CTRL/C trapping.  

                Note:   If  the routine is reentered (because CTRL/C was
                typed during the execution of function()),  the  program
                aborts.  

        Bugs 

                Runs on RSTS/E RT11 mode only.  


[[        C Compiler and Library]]                                    Page 5-197
        setjmp  Execute non-local goto


        5.153  Execute non-local goto                _______ _________ ____



                                   **********
                                   * setjmp *
                                   **********



        File name:      setjmp.mac


        Usage

                #include <setjmp.h>

                setjmp(env);
                jmp_buf         env;    /* Static save buffer   */

                longjmp(env, val)
                jmp_buf         env;    /* Was set by setjmp    */
                int             val;    /* Value to return      */

        Description:

                These  routines  are  useful for dealing with errors and
                interrupts encountered in a low-level  subroutine  of  a
                program.  

                Setjmp()  saves  its  stack environment in env for later
                use by unwind().  It returns 0.  

                Longjmp(env)  restores the environment saved by the last
                call of setjmp(env).  It then returns in such a way that
                execution  continues as if the call of setjmp() had just
                returned.  All accessible data have  values  as  of  the
                time  setjmp()  was  called.   The return from setexit()
                will have the specified value.  For example:  

                    #include <setjmp.h>
                    jmp_buf     env;
                    ...
                    main() {
                        ...
                        if (setjmp(&env) != 0) {
                            err_exit(); /* Longjmp called       */
                        }
                        else {
                            process();  /* Setjmp  called       */
                        }
                        ...
                    process() {
                        ...

[[        C Compiler and Library]]                                    Page 5-198
        setjmp  Execute non-local goto


                        longjmp(&env);

                The  routine  that  called setjmp() must still be active
                when longjmp() is called.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-199
        sleep   Delay job a given number of seconds


        5.154  Delay job a given number of seconds                _____ ___ _ _____ ______ __ _______



                                    *********
                                    * sleep *
                                    *********



        File name:      sleep.mac


        Usage

                sleep(delay);
                int             delay;

        Description

                Sleep a specified number of seconds.  

        Bugs 

                On RSTS/E, the reader should refer to the description of
                SLEEP() in the operating system documentation.  

                On  native  RSX-11M  or  RSX  emulated  by  VMS, sleep()
                executes a mark-time (MRKT$) and  wait  sequence,  using
                event flag 1.  

                On  native  RT11,  sleep()  executes  a .TWAIT executive
                request.  

                Sleep flushes stdout and stderr.  


[[        C Compiler and Library]]                                    Page 5-200
        sprintf Formatted Numeric Conversion


        5.155  Formatted Numeric Conversion                _________ _______ __________



                                   ***********
                                   * sprintf *
                                   ***********



        File name:      sprint.mac


        Usage

                char *
                sprintf(buffer, format, arg1, ...);
                char            *buffer;
                char            *format;

        Description

                sprintf()  converts  and  formats its arguments, writing
                the result to the indicated string buffer.  

                For  information  on  formatting,  please  refer  to the
                description of printf.  

                sprintf()  returns  a pointer to the EOS byte at the end
                of the output buffer.  Note, however, that this  feature
                is not transportable to other C implementations.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-201
        sscanf  Formatted input conversion


        5.156  Formatted input conversion                _________ _____ __________



                                   **********
                                   * sscanf *
                                   **********



        File name:      sscanf.mac


        Usage

                sscanf(buf, fmt, pointer(s))
                char            *buf;   /* Output buffer        */
                char            *fmt;   /* Format string        */

        Description

                sscanf()  parses  the input string, in buf, according to
                the indicated format descriptor, storing the results  in
                the   pointer  arguments.   It  returns  the  number  of
                successfully assigned input items.  

                See    the    description   of   scanf()   for   further
                documentation.  

        Diagnostics 

                Sscanf()  returns  -1 if the end of the input string was
                detected and no data was stored.  It  returns  -2  if  a
                palpably incorrect format, such as "%" is encountered.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-202
        strcat  String Concatenate


        5.157  String Concatenate                ______ ___________



                                   **********
                                   * strcat *
                                   **********



        File name:      strcat.mac


        Usage

                char *
                strcat(out, in);
                char            *out;
                char            *in;

        Description

                Append "in" to "out".  Return out.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-203
        strchr  Find First Instance of a Character in a String


        5.158  Find First Instance of a Character in a String                ____ _____ ________ __ _ _________ __ _ ______



                                   **********
                                   * strchr *
                                   **********



        File name:      strchr.mac


        Usage

                char *
                strchr(stng, chr)
                char            *stng;  /* String to search in  */
                char            chr;    /* Byte to search for   */

        Description

                If  chr  is  in  stng,  return a pointer to it.  If not,
                return NULL.  

                See also index().  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-204
        strcmp  String Compare


        5.159  String Compare                ______ _______



                                   **********
                                   * strcmp *
                                   **********



        File name:      strcmp.mac


        Usage

                int
                strcmp(s1, s2);
                char            *s1;
                char            *s2;

        Description

                Compare two strings, returning 
                        -1 if s1  < s2
                         0 if s1 == s2
                        +1 if s1  > s2

        Bugs


[[        C Compiler and Library]]                                    Page 5-205
        strcpy  String copy


        5.160  String copy                ______ ____



                                   **********
                                   * strcpy *
                                   **********



        File name:      strcpy.mac


        Usage

                char *
                strcpy(out, in);
                char            *out;
                char            *in;

        Description

                Copy "in" to "out".  Return out.  

        Bugs 

                It might be more useful if it returned out + strlen(in).
                (See cpystr()).  


[[        C Compiler and Library]]                                    Page 5-206
        streq   String Equality Test


        5.161  String Equality Test                ______ ________ ____



                                    *********
                                    * streq *
                                    *********



        File name:      streq.mac


        Usage

                streq(a, b);
                char            *a;
                char            *b;

        Description

                Return TRUE if the strings are equal.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-207
        strlen  String length


        5.162  String length                ______ ______



                                   **********
                                   * strlen *
                                   **********



        File name:      strlen.mac


        Usage

                int
                strlen(s);
                char            *s;

        Description

                Return the length of the argument string.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-208
        strncat String Concatenate


        5.163  String Concatenate                ______ ___________



                                   ***********
                                   * strncat *
                                   ***********



        File name:      strnca.mac


        Usage

                char *
                strncat(out, in, count);
                char            *out;
                char            *in;
                unsigned int    count;

        Description

                Append  "in"  to  "out".   Return out.  At most, "count"
                bytes are moved from in.  Note  that  "count"  does  not
                include the trailing null.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-209
        strncmp String Compare With Count


        5.164  String Compare With Count                ______ _______ ____ _____



                                   ***********
                                   * strncmp *
                                   ***********



        File name:      strncm.mac


        Usage

                int
                strncmp(s1, s2, count);
                char            *s1;
                char            *s2;
                unsigned int    count;

        Description

                Compare   at  most  count  bytes  between  two  strings,
                returning:  

                        -1 if s1  < s2
                         0 if s1 == s2
                        +1 if s1  > s2

        Bugs


[[        C Compiler and Library]]                                    Page 5-210
        strncpy String Copy With Count


        5.165  String Copy With Count                ______ ____ ____ _____



                                   ***********
                                   * strncpy *
                                   ***********



        File name:      strncp.mac


        Usage

                char *
                strncpy(out, in, count);
                char            *out;
                char            *in;
                unsigned int    count;

        Description

                Copy "in" to "out".  Return out.  At most, "count" bytes
                are moved from  in.   Note  that  "count"  includes  the
                trailing null.  

                If strlen(in) is less than count, "out" is null-filled. 

                If  strlen(in)  is greater than count, the output buffer
                will not be null-trailed.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-211
        strneq  String Equality Test With Count


        5.166  String Equality Test With Count                ______ ________ ____ ____ _____



                                   **********
                                   * strneq *
                                   **********



        File name:      strneq.mac


        Usage

                int
                strneq(s1, s2, count);
                char            *s1;
                char            *s2;
                unsigned int    count;

        Description

                Compare   at  most  count  bytes  between  two  strings,
                returning TRUE if the the strings are equal.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-212
        strrchr Find Last Instance of a Character in a String


        5.167  Find Last Instance of a Character in a String                ____ ____ ________ __ _ _________ __ _ ______



                                   ***********
                                   * strrchr *
                                   ***********



        File name:      strrch.mac


        Usage

                char *
                strrchr(stng, chr)
                char            *stng;  /* String to search in  */
                char            chr;    /* Byte to search for   */

        Description

                If  chr  is  in  stng,  return  a  pointer  to  the last
                (rightmost) occurrance of it.  If not, return NULL.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-213
        swabb   Byte swap (argument is a buffer pointer)


        5.168  Byte swap (argument is a buffer pointer)                ____ ____ _________ __ _ ______ ________



                                    *********
                                    * swabb *
                                    *********



        File name:      swabb.mac


        Usage

                swabb(buffer);
                char            *buffer;

        Description:

                Return   buffer[0]   and  buffer[1]  as  a  byte-swapped
                integer.  Buffer need not be on any particular  byte  or
                word boundary.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-214
        swabi   Byte swap, (argument is an integer)


        5.169  Byte swap, (argument is an integer)                ____ _____ _________ __ __ ________



                                    *********
                                    * swabi *
                                    *********



        File name:      swabi.mac


        Usage

                swabi(value);
                int             value;

        Description

                Return value byte-swab'ed.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-215
        time    Compute time of day


        5.170  Compute time of day                _______ ____ __ ___



                                    ********
                                    * time *
                                    ********



        File name:      time.mac


        Usage


                long
                time(0);

                long
                time(tloc);
                long            *tloc;

          Internal

                call    $$time

        Description

                time  returns  the  time  of day in seconds.  If tloc is
                non-null, the return value is also stored in  the  place
                to which tloc points.  

                The  value  is  the  time  since  midnite,  Jan 1, 1970,
                measured in seconds.  

        Note 

                If  time()  appears  to give the wrong value, check that
                you have declared it 

                    extern long time();

        Internal

                $$time is called by time and ftime.  It returns the time
                value in registers r0 and r1, and the number of ticks in
                the current second in r2.  R3 and r4 are modified.  

                On RSX, $$time refreshes $$tick.  

        Bugs 

                The  Unix  time  function  returns  GMT.   This function

[[        C Compiler and Library]]                                    Page 5-216
        time    Compute time of day


                returns local time.  

                The leap year algorithm is only accurate in the range 

                        1970 <= year < 2100


[[        C Compiler and Library]]                                    Page 5-217
        toascii Convert to 7-bit Ascii


        5.171  Convert to 7-bit Ascii                _______ __ _____ _____



                                   ***********
                                   * toascii *
                                   ***********



        File name:      toasci.mac


        Usage

                toascii(c);
                int             c;

        Description

                Remove the parity bit from c.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-218
        tod     Compute time of day


        5.172  Compute time of day                _______ ____ __ ___



                                     *******
                                     * tod *
                                     *******



        File name:      tod.mac


        Usage


                long
                tod(0);

                long
                tod(tloc);
                long            *tloc;


        Description

                tod()  returns  the  time of day in seconds.  If tloc is
                non-null, the return value is also stored in  the  place
                to which tloc points.  

                tod()  is  fairly fast.  time() computes the "Unix time"
                but is much slower and larger.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-219
        tolower Convert upper-case to lower-case


        5.173  Convert upper-case to lower-case                _______ __________ __ __________



                                   ***********
                                   * tolower *
                                   ***********



        File name:      tolowe.mac


        Usage

                tolower(c);
                int             c;

        Description

                If  c is a upper-case alphabetic, return it's lower-case
                equivalent.  Otherwise, return c.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-220
        toupper Convert lower-case alphabetic to upper-case


        5.174  Convert lower-case alphabetic to upper-case                _______ __________ __________ __ __________



                                   ***********
                                   * toupper *
                                   ***********



        File name:      touppe.mac


        Usage

                toupper(c);
                int             c;

        Description

                If  c is a lower-case alphabetic, return it's upper-case
                equivalent.  Otherwise, return c.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-221
        trace   Profile support entry module (with trace)


        5.175  Profile support entry module (with trace)                _______ _______ _____ ______ _____ ______



                                    *********
                                    * trace *
                                    *********



        File name:      pcsv.mac


        Usage

                #include <stdio.h>
                extern  FILE    *$$flow;

                $$flow = fopen("trace.out", "w");

                /* or $$flow = stderr; to trace to the console  */
                ...
                $$flow = NULL;          /* Turn off flow trace  */

          Internal

                jsr     r5,pcsv$
                .word   name            ; Pointer to name

                Where name has the structure:

                name:   .word   0       ; Counter
                        .asciz  /name/  ; function name

        Description

                This  module  is  called  whenever  a  function that was
                compiled with the profile option is executed.  It checks
                that  the  stack  will  remain  above 600 octal when the
                function executes and optionally prints a flow-trace.  

                If  $$flow  is  set  to  a file descriptor, the function
                name, location the function  is  called  from,  and  the
                calling  environment,  are  printed  on  each  call to a
                function compiled with the profile option.  

                The output format is:  

                        function_name<TAB>caller<TAB>environment

                Where  function_name  is  the name of the function being
                called, caller is the address  of  the  calling  program
                (actually,  the  return address), and environment is the
                R5 argument pointer (for  local  addressing  within  the

[[        C Compiler and Library]]                                    Page 5-222
        trace   Profile support entry module (with trace)


                routine  being called).  The information will be written
                to $$flow with a newline before and after.  

                If  profiling has been enabled and the program exits via
                error() or via an  operating-system  trap  (such  as  an
                illegal   memory   reference),   a   register  dump  and
                subroutine trace will be written to stderr.  

                See the description of calltrace() for details.  

        Internal 

                See csv$ for details of the calling environment.  

                When this routine is entered for the first time, it sets
                up to intercept synchronous system traps, and loads  the
                error  exit  address  and  profile  pointer.   The  trap
                service routines are in the  "traps"  module.   See  the
                description there for more information.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-223
        traps   Operating system trap handlers


        5.176  Operating system trap handlers                _________ ______ ____ ________



                                    *********
                                    * traps *
                                    *********



        File name:      traps.mac


        Usage

            Internal

                $$sstt::                ; RSX synchronous trap
                                        ; vector

                $$t410::                ; RT11 Entry after traps
                                        ; to vectors 4 and 10

        Description

                This  module  contains  code  which  is executed after a
                synchronous trap is detected by  the  operating  system.
                All  such  traps  are  regarded  as fatal errors and the
                program will be terminated.  

                This  code is enabled by executing any function, such as
                main(),  for  which  profiling  was  enabled  when   the
                function was compiled.  

                The following traps are processed:  

                        Illegal memory reference (trap through vector 4)
                        Illegal instruction (trap through vector 10)
                        BPT (assuming a debugging aid is not present)
                        IOT
                        Illegal TRAP (this may be a Fortran error)
                        Illegal EMT (RSX only)
                        Floating point exception (RSX only)
                        Memory management violation

                Before exiting to the operating system, the registers at
                the time the trap occurred will be written, in octal, to
                stdout.   Note  also  that  a calling sequence traceback
                will be written to stdout by error().  

                If  a  trap  occurred,  the  program  will  exit  to the
                operating system with a "severe error" status.  

                Note  that some errors, such as stack overflow or random

[[        C Compiler and Library]]                                    Page 5-224
        traps   Operating system trap handlers


                jumps into the operating system, may cause the C program
                to   be  terminated  without  the  C  library  regaining
                control.  

            Internal 

                The  first  call  to  pcsv$ will initialze trapping.  On
                RSX11-M, the SVTK$ executive service will be called.  On
                RT11,  the .tprset monitor request will be executed.  As
                .trpset only traps illegal memory reference (trap to  4)
                and   illegal   instruction  (trap  to  10),  the  other
                interesting  vectors   are   initialized   by   absolute
                references (.ASECT).  

        Diagnostics 

        Bugs 

            Internal 

                Don't   forget   to   handle  floating-point  when  it's
                implemented.  


[[        C Compiler and Library]]                                    Page 5-225
        ungetc  Push back a character onto an input file


        5.177  Push back a character onto an input file                ____ ____ _ _________ ____ __ _____ ____



                                   **********
                                   * ungetc *
                                   **********



        File name:      ungetc.mac


        Usage

                ungetc(c, iop);
                char            c;
                FILE            *iop;

        Description

                Push one character back on the indicated stream.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-226
        unwind  Execute non-local goto


        5.178  Execute non-local goto                _______ _________ ____



                                   **********
                                   * unwind *
                                   **********



        File name:      unwind.mac


        Usage

                setexit();

                unwind();

        Description:

                These  routines  are  useful for dealing with errors and
                interrupts encountered in a low-level  subroutine  of  a
                program.  

                setexit()  saves its stack environment in a static place
                for later use by unwind().  It returns 0.  

                Unwind() restores the environment saved by the last call
                of setexit().  It  then  returns  in  such  a  way  that
                execution continues as if the call of setexit() had just
                returned.  All accessible data have  values  as  of  the
                time  unwind()  was  called.   The return from setexit()
                will have the value 1.  For example:  

                        if (setexit()) {
                                        /* Unwind called        */
                        }
                        else {
                                        /* Setexit setup called */
                        }

                The  routine  that called setexit() must still be active
                when unwind() is called.  

        Bugs 

                Obsolete -- use setjmp/longjmp instead.  


[[        C Compiler and Library]]                                    Page 5-227
        wdleng  Expensive way to say sizeof(int)


        5.179  Expensive way to say sizeof(int)                _________ ___ __ ___ ___________



                                   **********
                                   * wdleng *
                                   **********



        File name:      wdleng.mac


        Usage

                wdleng()

        Description

                Return word length in bits.  

        Bugs 

                Assuming 8-bit bytes, this may be replaced by:  

                        #define wdleng() (sizeof (int) * 8)



[[        C Compiler and Library]]                                    Page 5-228
        wrapup  Dummy routine called on exit


        5.180  Dummy routine called on exit                _____ _______ ______ __ ____



                                   **********
                                   * wrapup *
                                   **********



        File name:      wrapup.mac


        Usage

                wrapup()

        Description

                This  routine  (which does nothing) is called on exit if
                the user's program does not provide a wrapup() routine. 

                Wrapup will be called only once.  

        Bugs 


[[        C Compiler and Library]]                                    Page 5-229
        zero    Clear a block of memory


        5.181  Clear a block of memory                _____ _ _____ __ ______



                                    ********
                                    * zero *
                                    ********



        File name:      zero.mac


        Usage

                zero(addr, nbytes);
                char            *addr;
                unsigned int    nbytes;

        Description:

                Clear the block of core.  No value is returned.  

        Bugs 














                                    CHAPTER 6

                              LIBRARY HEADER FILES



        This  chapter contains descriptions of the standard header files
        that are  used  by  C  programs  and  libraries.   In  addition,
        descriptions of internal routines are provided.  

        These   files   are   included  in  your  program  source  by  a
        pre-processor command of the form:  

                #include <filename.h>


[[        C Compiler and Library]]                                      Page 6-2
        Software Support Manual


        6.1  Character test macros and global definitions              _________ ____ ______ ___ ______ ___________



                                    *********
                                    * ctype *
                                    *********



        File name:      ctype.h 



        NAME:   ctype -- Character test macros and global definitions 

        SYNOPSIS:  

                #include <ctype.h> 

        DESCRIPTION:  

                This   module  defines  a  set  of  character  test  and
                manipulation macros (or, on  Decus  C,  functions)  that
                allow   classification   and   modification   of   Ascii
                characters.  If the  C  compiler  supports  macros  with
                arguments, the following are defined:  

                  isupper(c)    /* Upper case alphabetic        */
                  islower(c)    /* Lower case alphabetic        */
                  isalpha(c)    /* Alphabetic in any case       */
                  isdigit(c)    /* Decimal digit                */
                  isalnum(c)    /* Alphabetic or digit          */
                  isxdigit(c)   /* Hexadecimal digit            */
                  isspace(c)    /* Space or tab                 */
                  ispunct(c)    /* Punctuation                  */
                  isgraph(c)    /* Visible character            */
                  isprint(c)    /* Printable character          */
                  iscntrl(c)    /* Control character            */
                  isascii(c)    /* 7-bit Ascii character        */
                  _toupper(c)   /* Lower case convert to Upper  */
                  _tolower(c)   /* Upper case convert to Lower  */
                  toascii(c)    /* Remove eighth (parity) bit   */

                Note  that  _toupper()  and  _tolower() must not be used
                with arguments that have side effects, such as 

                        _toupper(*ptr++);

                Use the functions toupper() and tolower() instead.  

        BUGS:  


[[        C Compiler and Library]]                                      Page 6-3
        fps     Bit definitions for the floating point status word


        6.2  Bit definitions for the floating point status word              ___ ___________ ___ ___ ________ _____ ______ ____



                                     *******
                                     * fps *
                                     *******



        File name:      fps.h 



        NAME:   fps  --  Bit  definitions  for the floating point status
                word 

        SYNOPSIS:  

                #include <fps.h> 

        DESCRIPTION:  

                This  module  defines  common  definitions for the FP-11
                floating point status word.  The following are defined: 

                FER     0100000 Floating error  (sense/reset)
                FID     0040000 Disable all interrupts
                FIUV    0004000 Interrupt on undefined variable
                FIU     0002000 Interrupt on underflow
                FIV     0001000 Interrupt on overflow
                FIC     0000400 Interrupt on int. conv. error
                FD      0000200 Double precision mode
                FL      0000100 Long integer mode
                FT      0000040 Chop mode
                FN      0000010 Floating negative (sense)
                FZ      0000004 Floating zero     (sense)
                FV      0000002 Floating overflow (sense)
                FC      0000001 Floating carry    (sense)



[[        C Compiler and Library]]                                      Page 6-4
        initial Specify Initializers and Finalizers


        6.3  Specify Initializers and Finalizers              _______ ____________ ___ __________



                                   ***********
                                   * initial *
                                   ***********



        File name:      initia.h 



        NAME:   initial -- Specify Initializers and Finalizers 

        SYNOPSIS:  

                 #include <initia.h>

                 INITIAL
                 { initial-code-block };

                 FINAL
                 { final-code-block };

        DESCRIPTION:  

                The macros defined in this module provide a facility for
                module-specific initialization  and  finalization  code.
                The code in the initial-code-block is called as a normal
                C   function   before    main()    is    called;     the
                final-code-block is called on exit, just after wrapup(). 

                Neither call passes any arguments.  

                Any  number  of  modules  in  an image may independently
                declare initializers or finalizers;  all of them will be
                called at startup or exit.  However, it is impossible to
                predict what order  the  calls  will  be  made  in,  and
                programs should not rely on any particular ordering.  

                A  typical  use  of  initializers  and finalizers is the
                following:  Suppose you have  a  package  that  supports
                access to some on-disk data base;  a user of the package
                will call a lookup and an  update  function.   The  file
                containing  the  data  base  must  be  opened before any
                operations on it can take place, and it should be closed
                when  the program is finished.  (Assume that the package
                maintains some sort of resident  buffer  which  it  must
                flush.) There are two conventional approaches to solving
                this problem:  Have  the  lookup  and  update  functions
                check  the file on each call, and open it if necessary -
                which could be quite expensive if they  are  very  small

[[        C Compiler and Library]]                                      Page 6-5
        initial Specify Initializers and Finalizers


                functions, and in any case does not solve the problem of
                properly closing the file - or  have  the  main  program
                call  an initialization and finalization function at the
                proper time.  The problem with this latter  approach  is
                lack  of modularity - the main program ought not to have
                to  know  that  the  module  needs   initialization   or
                finalization.  

                The solution using these macros is straightforward.  The
                defining module includes the calls:  

                        INITIAL
                        { open-the-data-base };

                        FINAL
                        { flush-buffers-and-close-the-data-base };

                The   wrapup()  function  is  treated  like  a  built-in
                finalizer;  however, it is guaranteed to execute  before
                any other finalizers.  (The module defining wrapup() may
                declare an initializer or finalizer if  it  wishes;   it
                will  be  treated  just  like all other initializers and
                finalizers.) 

                If any finalizer (or wrapup()) calls exit(), the program
                exits immediately.  

                Notes:   Using  INITIAL  will  declare a static function
                named $init$(), and a (char *) named $init_;  similarly,
                FINAL  will  declare  $finl$()  and  $finl_.  Also, both
                INITIAL and FINAL  generate  dsect  commands.   Since  C
                provides  no  way  to "remember" the current dsect, both
                macros issue a dsect ""  command  when  they  are  done,
                restoring the C default dsect.  

                While  it  is  a poor idea to write code that depends on
                the order  in  which  initializers  and  finalizers  are
                executed,  this  can  be  useful information to have for
                debugging.  Execution is always in the  order  that  the
                modules  involved  were  examined by the task builder or
                linker.  When the modules  are  named  explicitly,  this
                will  just  be the order in which they were named.  When
                the modules come from a library, it  will  be  extremely
                difficult  to  predict  the  order in which they will be
                extracted and linked in.  

                Warning:  While initializers and finalizers provide some
                modularity to package initialization  and  finalization,
                they are not a panacea.  For example, if package A calls
                routines in package B from within its initializers,  and
                package   B  also  declares  initializers,  the  correct
                functioning of a program that includes both - hence,  of
                any program using package A - will be problematical.  


[[        C Compiler and Library]]                                      Page 6-6
        initial Specify Initializers and Finalizers


        INTERNAL:  

                The  macros  operate  by leaving a list of (pointers to)
                functions to be called in psects $INIT$ and $FINL$.   In
                order  to  be able to determine the beginning and end of
                these psects,  the  psects  $INIT,  $FINL,  $INIT.,  and
                $FINL.,  are  also  reserved.   These  psects  must  not
                actually contain any data;  they exist solely to provide
                well-defined   endpoints   to   the  initialization  and
                finalization  list.   The  names  are   consecutive   in
                alphabetical  sequence,  so  the Task Builder will place
                them in order.  The RT11 Linker, however - and the  Task
                Builder  with the /SQ switch - place psects in the order
                they are encountered.  Since it  impossible  to  predict
                what  order  the  various  modules  will  be seen by the
                linking program, it is essential that EVERY module  that
                refers  to  any of these psects refer to the two related
                ones as well, and in the correct order.  

        BUGS:  

                Requires  the  DECUS  C  dsect  commands;   hence,  very
                non-portable.  It may be possible to  provide  the  same
                functionality   using  different  techniques;   if  not,
                what's wrong with your implementation?  

        AUTHOR:  

                Jerry Leichter 


[[        C Compiler and Library]]                                      Page 6-7
        rtime   Define time buffer structure for $$rtime()


        6.4  Define time buffer structure for $$rtime()              ______ ____ ______ _________ ___ _________



                                    *********
                                    * rtime *
                                    *********



        File name:      rtime.h 



        NAME:   rtime -- Define time buffer structure for $$rtime() 

        SYNOPSIS:  

                #include <rtime.h> 
                   ...
                struct TIME buffer;  

        DESCRIPTION:  

                This  header  file  defines  the  structure  of the time
                buffer used by the standard library  $$rtime()  function
                (which is unique to Decus C).  It is defined as follows: 

                struct TIME {
                        int     year;           G.TIYR  year - 1900
                        int     month;          G.TIMO  Jan. = 1
                        int     day;            G.TIDA
                        int     hour;           G.TIHR  00 .. 23
                        int     minute;         G.TIMI  00 .. 59
                        int     second;         G.TISC  00 .. 59
                        int     tick;           G.TICT  00 .. tsec-1
                        int     tsec;           G.TICP  tick/second
                };  

        BUGS:  

                Oboslete, use time() and localtime() instead.  


[[        C Compiler and Library]]                                      Page 6-8
        setjmp  Define buffer for setjump() and longjump()


        6.5  Define buffer for setjump() and longjump()              ______ ______ ___ _________ ___ __________



                                   **********
                                   * setjmp *
                                   **********



        File name:      setjmp.h 



        NAME:   setjmp -- Define buffer for setjump() and longjump() 

        SYNOPSIS:  

                #include <setjmp.h> 

        DESCRIPTION:  

                This  defines  the  jmp_buf  array  that is used for the
                setjmp() and longjmp() functions.  

        BUGS:  


[[        C Compiler and Library]]                                      Page 6-9
        stdio   Definitions for standard i/o library


        6.6  Definitions for standard i/o library              ___________ ___ ________ ___ _______



                                    *********
                                    * stdio *
                                    *********



        File name:      stdio.h 



        NAME:   stdio -- Definitions for standard i/o library 

        SYNOPSIS:  

                #include <stdio.h> 

        DESCRIPTION:  

                <stdio.h>  should  be  included in the assembly of all C
                programs that use the  standard  i/o  library  (fopen(),
                getc(), printf(), etc.) 

                It defines the following:  

                  FILE  The  i/o  routines  use  and  return pointers to
                        objects of this type.

                  NULL  I/O routines signal "rejection" by  returning  a
                        null pointer.

                  EOF   The get character routine returns this value  to
                        signal end of file.

                  TRUE  The value 1.

                  FALSE The value 0.

                  EOS   The "end of string" marker: '\0'.

                  IO_SUCCESS Normal exit to operating system.  

                  IO_WARNING "Warning error" exit to operating system.  

                  IO_ERROR   "Error" exit to operating system.  

                  IO_FATAL   "Severe error" exit to operating system.  

                stdin   The "standard" input file.  Normally the user's 
                        terminal; it may be redirected.


[[        C Compiler and Library]]                                     Page 6-10
        stdio   Definitions for standard i/o library


                stdout  The "standard" output file.  Normally the user's 
                        terminal; it may be redirected.

                stderr  The "error" output file.  It will always write 
                        to the user's terminal.

        DIFFERENCES FROM UNIX:  

                FILE  is  defined  as  a  "typedef struc", rather than a
                #define.  The i/o structure  is  considerably  different
                from  Unix.  It is, however, arranged so that reasonable
                compatibility may  be  attained.   Specifically,  things
                which  have the same name are used for the same purpose,
                and located in the same place within the I/O structure. 

        ACCESSING THE FDB ON RSX MODES:  

                The  FDB  (file  data  block)  is  the  primary means of
                communication between the C I/O library and the RSX file
                control  services  modules.  It contains file and record
                format information as well as pointers and counters  for
                accessing  data  in  the file.  It is highly recommended
                that  you  do  not  access  this  information  directly.
                Should you need to do so, the following may be done:  

                  extern char *F_RTYP;  /* F.RTYP (char) in fdb */
                  extern char *F_SEQN;  /* F.SEQN  (int) in fdb */
                  ...
                  fd = fopen("file.nam", "r");
                  /*
                   * Set rtyp to the record type, stored as a
                   * byte at offset F.RTYP
                   */
                  rtyp = fd->io_fdb[(int) &F_RTYP] & 0377;
                  /*
                   * set seqn to the sequence number (printfile
                   * fixed header), stored as an integer at
                   * offset F.SEQN.
                   */
                  seqn = *((int *) &fd->io_fdb[(int) &F_SEQN]);

                The  somewhat  messy  use of casts and addressing allows
                the program to use the value of F.xxx stored in the  RSX
                system library.  

        BUGS:  

                TRUE,  FALSE,  and  EOS  are not present in <stdio.h> on
                some other C systems.  

                If  you  compile with the /r switch (-r on RSX modes) or
                #define rsts before #include <stdio.h>, a native  RSTS/E
                I/O  vector  will  be  defined  which  is  neither fully
                supported nor fully implemented.  

[[        C Compiler and Library]]                                     Page 6-11
        stdio   Definitions for standard i/o library




[[        C Compiler and Library]]                                     Page 6-12
        time    Define time buffer structure for localtime()


        6.7  Define time buffer structure for localtime()              ______ ____ ______ _________ ___ ___________



                                    ********
                                    * time *
                                    ********



        File name:      time.h 



        NAME:   time -- Define time buffer structure for localtime() 

        SYNOPSIS:  

                #include <time.h> 
                   ...
                extern struct tm *localtime();  

        DESCRIPTION:  

                This  header  file  defines  the  structure  of the time
                buffer  used  by  the   standard   library   localtime()
                function.  It is defined as follows:  

                struct tm {
                  int   tm_sec;         /* Seconds              */
                  int   tm_min;         /* Minutes              */
                  int   tm_hour;        /* Hours                */
                  int   tm_mday;        /* Day in month         */
                  int   tm_mon;         /* Month                */
                  int   tm_year;        /* Year                 */
                  int   tm_wday;        /* Weekday              */
                  int   tm_yday;        /* Days since Jan 1     */
                  int   tm_isdst;       /* Daylight Savings = 1 */
                };  

                extern struct tm *localtime();  

        BUGS:  

                Unix V7 changed the tm_isday to tm_isdst.  Thanks guys. 


[[        C Compiler and Library]]                                     Page 6-13
        timeb   Define timeb buffer structure for ftime()


        6.8  Define timeb buffer structure for ftime()              ______ _____ ______ _________ ___ _______



                                    *********
                                    * timeb *
                                    *********



        File name:      timeb.h 



        NAME:   timeb -- Define timeb buffer structure for ftime() 

        SYNOPSIS:  

                #include <timeb.h> 
                   ...
                extern long ftime();  

        DESCRIPTION:  

                This  header  file  defines  the  structure of the timeb
                buffer used by the standard  library  ftime()  function.
                It is defined as follows:  

                struct timeb {
                  long          time;
                  unsigned      milltim;
                  short         timezone;
                  short         dstflag;
                };  

                The time value is identical to the value returned by the
                time() function.  Milltim is the number of  milliseconds
                in the current second.  Timezone indicates the number of
                minutes past GMT in the  current  time  zone  (zero  for
                Decus  C) and dstflag is set if Daylight Savings Time is
                in effect.  














                                   APPENDIX A

                                 IMPLEMENTATION





        A.1  Overview              ________

        This  document  describes the Decus C distribution and discusses
        its implementation on RSTS/E, RSX-11M, RT-11, and VAX/VMS.  


        A.2  Distribution              ____________



                                      NOTE

             The  following  is  in  a  state  of change.  The most
             likely strategy is to have several kits:  

                  1.  VMS  backup format at 1600 bpi built on a VMS
                      V3.2 system.  This will contain  both  source
                      and compiled images.  

                  2.  DOS  (FLX)  format  (source only) on two 1200
                      foot magtapes at 800 or 1600 bpi.  This  will
                      contain source files only.  

                  3.  RT11  RL02 disk containing a built system and
                      sources stored in "archive" format.  

                  4.  RT11  RX01  disk containing built images only
                      -- no sources.  

             Suggestions for improvements are welcome.  


        The  master  source  tape  (DOS  FLX) was generated on a VAX/VMS
        system.  All files contain readable Ascii text.  All  executable
        images were generated by supplied command files.  

        The compiler and run-time library, accounts [5,1] through [5,7],
        comprise a compiler and run-time system for the C language.  The

[[        C Compiler and Library]]                                      Page A-2
        Getting on the Air with Decus C


        compiler was written by David G.  Conroy, and modified by Martin
        Minow, Robert B.  Denny, Clifford Geshke,  and  several  others.
        The  run-time  libraries  for  RSX-11M and RT-11 were written by
        Martin Minow with help from many friends.   In  addition,  there
        are  several  executive interface libraries:  one for RSX-11M by
        Robert B.  Denny, one for RSTS/E by Jim  Burrows,  and  one  for
        Vax/VMS (for interface with Vax-11 C) by Martin Minow.  

        There is also a portable math library by Fred Fish.  

        The  program  library,  accounts  [6,1]  through [6,7], offers a
        collection of tools, games, and other programs,  mostly  written
        in  C.   They  are  not  needed for installation of the compiler
        (although several programs in the tools account, such  as  KWIK,
        are  used to build the documentation.) In general, you should be
        aware that only the tools in [6,1] are tested.  

        The distribution account numbers were originally chosen so as to
        be identical under RSX-11M (octal) and RSTS/E (decimal).  If the
        C  language  system  is  not  stored  in the above accounts, the
        implementor on RSTS/E will have to edit command files to  define
        the  proper  accounts.   The  GETCMD  and  BUILD programs may be
        useful in this regard.  

            [5,1] Command procedures, documentation source, etc.
            [5,2] Documentation.
            [5,3] Compiler and assembler source.
            [5,4] Common (non-I/O) library source.
            [5,5] I/O library source and command files.
            [5,6] Native RSTS/E interface library.
            [5,7] Native RSX-11M interface library.

            [6,1] "Software tools."
            [6,2] Miscellaneous programs -- games and stuff.
            [6,3] Cross-assemblers for several micro-computers.
            [6,4] Lexical analyser generator.
            [6,5] Pieces of a standard library in C
            [6,6] Useful subroutines in C.
            [6,7] Vax/VMS interface library.

        The  two-tape distribution contains accounts [5,*] on one (full)
        tape and accounts [6,*] on the second (2/3 full) tape.  

        Each  account  contains  a  file named README.nnn describing the
        contents of the  account.   For  example,  the  README  file  in
        account [5,1] is named README.501.  


        A.3  Command File Conventions              _______ ____ ___________

        Command  files used to build the C compiler and run-time library
        follow the following standard:  

            V?????  VAX/VMS indirect command file 

[[        C Compiler and Library]]                                      Page A-3
        Getting on the Air with Decus C



            X?????  RSX-11M file for the RSTS/E RSX emulator 

            R?????  RT-11   file for the RSTS/E RT-11 emulator 

            M?????  RSX-11M indirect command file 

            T?????  RT-11   indirect command file 

            .CMD    RSTS/E  indirect  command  files,  RSX-11M  indirect
                    command  files,  and  indirect  command  files   for
                    MAC.TSK and MACRO.SAV.  

            .COM    RT-11 or VMS indirect command files 

            .TKB    Task-builder indirect command files 

            .ODL    Task-builder overlay descriptor commands 

            .EIS    [RT11.EIS only] hardware EIS configuration 

        Command  files  used  to  build  tools  and C-language libraries
        follow the following convention:  

            VN????  Use the native Vax-11C compiler only.  

            VX????  Use Decus-C (RSX compatibilitye) on Vax/VMS.  

            VB????  Use   either,  selecting  the  compiler  at  command
                    invocation.  

            RX????  RSTS/E RSX-11M emulation mode.  

            RT????  RSTS/E RT-11 emulation mode.  

            M????   RSX-11M native.  

            T????   RT-11 native.  



        A.4  Distribution Contents in Detail              ____________ ________ __ ______


        [5,1] [.command] Command Files and Documentation 

                This account contains documentation source files (.rno),
                kit building command files, and a few things that didn't
                fit   anywhere   else.    This   includes  a  number  of
                special-purpose command files  used  to  develop  the  C
                language   system  (such  as  FORK.COM,  BATCH.COM,  and
                TOOL.COM) which may serve as models for your own  needs.
                It also contains the source for CRUN.BAS, used on RSTS/E
                systems to pass arguments to C programs and  source  for

[[        C Compiler and Library]]                                      Page A-4
        Getting on the Air with Decus C


                CCN,  used to compile and assembler C programs on native
                RSX-11M.  

                A  full  build  of the Decus C system may be effected by
                executing RBUILD.CMD on RSTS/E (requires privileges)  or
                VBUILD.COM  on  VAX/VMS.   Either command requires about
                two hours to complete.  At least  2000  free  blocks  of
                disk  space  is  necessary on the default (public) disk.
                Note that the build will abort if the  RSX  LBR  or  TKB
                programs cannot obtain sufficient contiguous disk space. 

                The  RGTDOC.CMD  or VGTDOC.COM command files build a new
                documentation kit.  To build the documentation,  proceed
                as follows:  

                1.  Build the compiler and libraries.  

                2.  Build the tools.  

                4.  Use  GETRNO  to  create  library runoff files -- see
                    VGTDOC.COM or RGTDOC.CMD.  

                5.  Use  RNO.TSK  to  build  documentation on RSX-11M or
                    RSTS/E, or use RUNOFF to built the  library  on  VMS
                    V2.0.  

                6.  If  on  RSTS/E or VMS, execute FIXDOC to repair .DOC
                    files  after  RNO.TSK  or  RUNOFF.EXE  has  finished
                    messing   them   up.    (See  the  gory  details  in
                    RGTDOC.CMD and VGTDOC.CMD.) 

                    The GETCMD.C and BUILD.C programs were used to build
                    command  files  for  compilation  and  network  file
                    transfer.   See  the  tool  documentation or examine
                    some command files for more  information.   Run-time
                    library   command   files   were   built  using  the
                    RLBCMD.CMD  (RSTS/E)  or  VLBCMD.COM  (VMS)  command
                    files.   Tool  command  files  were  built using the
                    BTOOLS.COM or RTOOLS.CMD command files.  

        [5,2]            RSTS/E only 

                On  some  distributions  (but not the Decus submission),
                this account contains the running system for RSTS/E  and
                save  images for RT-11.  It is never needed on VMS.  Any
                file residing in this account has  been  generated  from
                source stored in other accounts.  

                The  VMS  kit  read/write  command  procedures reference
                account [5,2] only to copy  documentation  to  and  from
                magtape.  Note that CC.DOC, AS.DOC, CBUGS.DOC, CLIB.DOC,
                and WIZARD.DOC are in this account on  all  distribution
                kits.  


[[        C Compiler and Library]]                                      Page A-5
        Getting on the Air with Decus C


                This  account  is  the  only one that may contain binary
                files.  Consequently,  the  RSX-11M  interface  library,
                CX.OLB,  is  stored  here.   It is needed only on native
                RSX-11M systems.  RSX-11M users should  be  warned  that
                CX.OLB  was  generated  on  a VAX/VMS system.  CX.OLB is
                built from a command file in [5,7].  

                Note  that  some subroutines will not assemble on RSTS/E
                or early versions of RSX-11M as  the  associated  macros
                are not present in the system macro library.  

        [5,3] [.comp]    Compiler source 

                This account contains the source and build files for the
                compiler (CC????.MAC), assembler (AS????.MAC),  and  the
                compiler support library (L?????.MAC).  

                The support library is a stripped-down variant of a very
                early  version  of  the  standard  library,   which   is
                conditionally  compiled  for  RSX  or  RT-11  flavor I/O
                support.  It is not particularily efficient.  

                To build the compiler, edit RSX.MAC and RT11.MAC to suit
                your particular hardware needs and execute the CC  build
                command file:  

                    @    VMAKCC.COM     On VMS
                    ATPK XMAKCC.CMD     On RSTS/E RSX mode
                    ATPK RMAKCC.CMD     On RSTS/E RT-11 mode
                    @    MMAKCC.CMD     On RSX native mode
                    @    TMAKCC.COM     On RT-11 native mode

                Then, build the assembler:  

                    @    VMAKAS.COM     On VMS
                    ATPK XMAKAS.CMD     On RSTS/E RSX mode
                    ATPK RMAKAS.CMD     On RSTS/E RT-11 mode
                    @    MMAKAS.CMD     On RSX native mode
                    @    TMAKAS.COM     On RT-11 native mode

        [5,4] [.otscom]  Common Library 

                This  account  contains  the  "common"  run-time library
                source.  These files have  no  I/O  or  operating-system
                dependencies.    (Note  that  a  few  reference  library
                routines to print error messages.) Several  modules  are
                called  by  direct  code generation sequences (e.g., the
                EIS support routines).   Command  files  are  stored  in
                [-.OTSIO] ([5,5]).  

        [5,5] [.otsio]   I/O library 

                This  account  contains  I/O  dependent run-time library
                source files.   These  files  conditionally  compile  to

[[        C Compiler and Library]]                                      Page A-6
        Getting on the Air with Decus C


                generate  code  for  either  RSX-11M  or RT-11 operating
                system support.   You  should  be  warned  that  several
                modules   contain   essentially   two  totally  distinct
                subroutines.    Internally-called   routines   are    in
                IO????.MAC.   INIT.MAC  contains  the  run-time  startup
                program,  which  is  very  system  dependent.   It  also
                contains  some  code  which  is  specific  to particular
                operating system releases.  

                To  build  a  library,  invoke  the  appropriate command
                procedure, using the format described above:  

                    @    VMAKLB.COM     On VMS
                    ATPK XMAKLB.CMD     On RSTS/E RSX mode
                    ATPK RMAKLB.CMD     On RSTS/E RT-11 mode
                    @    MMAKLB.CMD     On RSX native mode
                    @    TMAKLB.COM     On RT-11 native mode

        [5,6] [.rstslb]  RSTS/E Interface Library 

                RSTS/E  operating-system  dependent subroutines allowing
                access to RSTS/E executive services by C programs.  Many
                are  written  in C.  They are not as well documented (or
                written) as they might be.  

        [5,7] [.rsxlib]  RSX-11/M Interface Library 

                An  interface  library  to the RSX-11M executive.  It is
                not known what parts of this  library  work  on  VMS  or
                RSTS/E  emulation modes.  This library will not assemble
                on RSTS/E V7.0 as the distributed system  macro  library
                lacks certain executive service macros.  

        [6,1] [.tools]   Software Tools 

                C  tools.   See  [.tools]readme.601  for  details.   The
                following command files are provided:  

                    V?TOOL.COM      Vax/VMS:   VNTOOL  uses  the  native
                                compiler VAX-11C;  VXTOOL uses Decus  C;
                                and VBTOOL allows selection of either.  

                    R?TOOL.CMD      RSTS/E:   RXTOOL  uses RSX emulation
                                mode, while RTTOOL uses  RT11  emulation
                                mode.  

                    TTOOL.COM       Native RT11.  

                    MTOOL.CMD       Native RSX-11M.  

                The  command  files  were built by executing BUILD.C for
                all tools.  It is highly recommended that, when you need
                to  recompile  a  tool, you build the command file using
                BUILD.  For example, to build a command file for GREP on

[[        C Compiler and Library]]                                      Page A-7
        Getting on the Air with Decus C


                your current operating system, you need only execute:  

                        build grep.c >grep.cmd 

                On VMS, the TOOL.COM command file may be used to build a
                tool by running BUILD to create a command file which  is
                then executed.  

                Note  that  the  RSTS  and VMS commands refer to logical
                devices (BIN:) that, on VMS, are defined  externally  to
                the build process.  

        [6,2] [.misc]    Toys and Other Stuff 

                Toys,   half   baked   ideas,   and  other  stuff.   See
                [.misc]readme.602  for  details.   Command   files   are
                provided  to  build  COOKIE  on RSTS/E and VMS.  Some of
                these files haven't been touched in years.  

        [6,3] [.cross]   Cross Assemblers 

                A  variety  of cross assemblers.  See [.cross]readme.603
                for details.  This account also contains a copy  of  the
                8080  C  compiler  printed  in Dr.  Dobbs Journal, March
                1980.  Again, little recent debugging.  

                Files  in this account are stored in archives.  To build
                a cross assembler, you should first extract the relevant
                files.  These have not been extensively tested.  

        [6,4] [.lex]     Lexical Analyser 

                A lexical-analyser generator written by Charles Forsyth.
                The standard build command files  will  create  compiler
                command files.  

        [6,5] [.libc]  Library in C 

                The first pieces of a "standard" library, implemented in
                C.  Currently, the str???  and is???   routines,  a  few
                floating-point  routines,  and some pieces of printf are
                present.  It is hoped that this account will  eventually
                replace [.OTSCOM] and most of [.OTSIO] in the future.  

                Note  that,  in  the  first  Decus  C distribution, this
                account contained  a  machine-independent  microcomputer
                cross  assembler.   Those routines are now stored in the
                "cross assembler" directory in an archive).  

        [6,6] [.useful]  Useful subroutines 

                A library of useful subroutines written in C.  

        [6,7] [.vaxlib]  VAX/VMS Interface Routines 

[[        C Compiler and Library]]                                      Page A-8
        Getting on the Air with Decus C



                Interface  routines  for use with Decus C programs which
                are being  transported  to  the  native  VMS  C  program
                product.   This library predated the released version of
                Vax-11  C  and  may  contain  modules  that  have   been
                superseded by the distributed Vax-11 C run-time library. 

                Decus  C tools must be linked together with this library
                in order to access routines, such as fwild(),  that  are
                not  present  in  the Vax-11 C library.  Note especially
                that the fact that a routine exists in this library  (or
                that a tool compiles under Vax-11 C) does not imply that
                the tool or routine has been  tested.   If  you  blindly
                install this library, you are asking for trouble.  


        A.5  Installation Overview              ____________ ________



                                     WARNING

             If  you  already have Decus C, please backup all files
             and zero all accounts before copying this distribution
             to  disk.   Several  files  that  were on the previous
             Decus distribution are not on this tape.  


        If you are installing C for the first time, you should print all
        "README.???"   files,   the   compiler    and    library/support
        documentation files, NEWS.DOC, CC.DOC and WIZARD.DOC (in [5,2]),
        RSX.MAC, RT11.MAC, RT11.EIS, and  the  command  files  for  your
        operating system.  


                                     WARNING

             The   RT11.MAC   and   RSX.MAC   command   files,   as
             distributed,  assume  the   existance   of   the   SXT
             instruction.   This instruction is not present on some
             early  models  of  the  PDP-11.   If  C  programs   or
             libraries  are  to  run  on  a  PDP-11/20,  PDP-11/04,
             PDP-11/05, or on a PDP-11/40 without  EIS,  the  macro
             header  files  must  be  edited  to  define C$$SXT = 0
             before building  the  compiler  or  library.   Beware,
             non-SXT  compilation  hasn't  been  tested for quite a
             while.  

             If  your  system  does  not have EIS, you can make "no
             EIS" standard by editing RSX.MAC and RT11.MAC  to  set
             symbol C$$EIS to zero.  

             The native RSX build command file inquires whether SXT
             and EIS defaults must be set.  

[[        C Compiler and Library]]                                      Page A-9
        Getting on the Air with Decus C


        A.5.1  Installation on RSTS/E                ____________ __ ______

        This  installation  procedure  presupposes RSTS/E V7.1 or later.
        If you are running on a V6 release, you will have  to  edit  the
        command  files, converting them to batch control files.  You may
        also  need  to  edit  SUPORT.MAC,   INIT.MAC,   FWILD.MAC,   and
        SBREAK.MAC  in the run-time library as these routines presuppose
        executive services that were added with the V7.0 release.  Decus
        C  does  not  require  "large  files"  or  other optional RSTS/E
        features.  

        While  the  C  compiler  and run-time libraries generally do not
        require privileges, you will need privileges to  perform  a  few
        installation-support functions:  

                Creating accounts.

                Copying files to a specific account.

                Installing CCL's and system-wide logicals.

        Create  the  various  accounts,  [5,1]  through  [5,8] and [6,1]
        through [6,7].  The accounts may be created on a  private  disk.
        Then, copy the distribution tape to these accounts:  

                PIP disk:[*,*]<40>=tape:[*,*] 

        File  CX.OLB may be in some distributions.  It is not needed for
        RSTS/E systems and should be deleted.  

        The  system  manager  should  add the following commands to your
        system startup command file (before executing RBUILD):  

                RUN $UTILTY
                ADD LOGICAL disk:[account] C    ! define C logical
                CCL XCC-=C:CC.TSK;0             ! RSX    CC compiler
                CCL XAS-=C:AS.TSK;0             ! RSX    AS assembler
                CCL CC-=C:CC.SAV;8220           ! RT-11  CC compiler
                CCL AS-=C:CC.SAV;8220           ! RT-11  AS assembler
                CCL CRUN-=C:CRUN.*;30000        ! Turn CCL to chain call
                EXIT

        where  "disk:[account]" is specified to suit your installation's
        needs.  It need not be [1,2].  



                                      NOTE

             C programs will not compile if you haven't added C: as
             a logical device as they use this  logical  to  locate
             system-wide header files.  



[[        C Compiler and Library]]                                     Page A-10
        Getting on the Air with Decus C


        The  CCL's  install  CC.SAV  and  AS.SAV  to  run in a 28 K-word
        partition.  The parameter value is constructed as "8192+K" where
        K is the number of K-words the software is to run in.  Note that
        these programs do not dynamically expand memory on RSTS/E.  

        The   "tools"   build  command  files  also  make  reference  to
        system-wide logical PUB:.  This may be assigned to [1,2] or some
        other  "public  library"  account.   If  you do not wish to edit
        these files, you should add PUB:  as a "system-wide logical." 

        Make  sure protection codes are set properly in the files in C:.
        You may also want to add CC.HLP and [6,1]CTOOLS.HLP to the  help
        facility.  Their format is compatible with the VMS help facility
        and must be edited for use on RSTS/E.  

        Installing  the  entire system using the [5,1]RBUILD.CMD control
        file requires about two hours on a lightly-loaded 11/70 system. 

        Note  that  RSTS/E  system  installation requires system manager
        privileges  in  order  to  install  CCL  commands,  system  wide
        logicals,  and  to create files in other accounts.  No C program
        requires <232> privileges for its operation.  

        If  your  system  manager  installs  the RSTS/E feature patch to
        permit cross-account file creates within the  same  project  and
        gives  you  a  [5,0]  and [6,0] account, it is possible to build
        Decus C without privileges.  The RBUILD command file  cannot  be
        run directly, however.  


        A.5.2  Installation on VMS                ____________ __ ___

        This  installation  procedure presupposes VMS V2.0 or later.  If
        you are running on an earlier release, you will have to edit the
        command files, replacing account assignments as needed.  

        If  you  are  running  on VMS V3.0 or later, you can restore the
        system from magtape (VAX BACKUP format).  

        If  your  Decus  C  distribution  was  in FLX format, create the
        various accounts and copy account  [5,1]  from  the  magtape  to
        account [.command]:  

                $    create/dir   disk:[decusc]        $   set   default
        disk:[decusc] 

        The  VMS  V2.0 file system supports relative directory access as
        follows:  

                [-.subdirectory] 

        means "move to the parent of the current directory and then down
        to the indicated subdirectory." This is analogous  to  the  Unix
        syntax 

[[        C Compiler and Library]]                                     Page A-11
        Getting on the Air with Decus C



                ../subdirectory 

        This  is  not  supported  in  earlier  releases  of VMS.  If not
        running under VMS V2.0 or later, you  will  have  to  edit  .COM
        files   accordingly.    In   any   case,  create  the  following
        sub-directories ([P,Pn] shows  the  correspondance  between  the
        tape directory and disk subdirectory):  

            [5,1]  [.command] Command files and documentation
            [5,2]  []         .DOC files
            [5,3]  [.comp]    Compiler source
            [5,4]  [.otscom]  Common (no i/o) run-time library
            [5,5]  [.otsio]   I/O run-time library
            [5,6]  [.rstslb]  RSTS/E library
            [5,7]  [.rsxlib]  RSX-11/M library

            [6,1]  [.tools]  C source for useful programs
            [6,2]  [.misc]   Various junk
            [6,3]  [.cross]  Cross-assemblers
            [6,4]  [.lex]    Lexical analyser
            [6,5]  [.cfloat] Floating point library
            [6,6]  [.useful] Useful subroutines
            [6,7]  [.vaxlib] Vax native library

        Set  [.command]  as your current default and copy [5,1]VRKIT.COM
        from the magtape to this account:  

                $ set default [.command]
                $ mount/foreign mta0:
                $ mcr flx sy:=mt0:[5,1]vrkit.com/do

        Now, edit file VRKIT.COM to suit your needs and execute it.  (If
        your distribution is on 1200  foot  magtapes,  you  should  copy
        VRKIT1.COM,  execute  it, then mount the second magtape on MTA0:
        and execute (after  eventual  editing)  VRKIT2.COM.   The  VRKIT
        command  procedure  copies all other files to the disk.  Because
        of the many rewinds, this  command  requires  several  hours  to
        complete.  

        An  alternate  distribution  for  VMS  systems only uses the MCR
        RMSBCK utility to write each subdirectory in a "container" file.
        The distribution tape is labelled "C" and contains the following
        files:  

                README.NOW      A short file explaining the process
                KIT.DOC         This document
                BCK.COM         The backup command file used
                RST.COM         A model restore command file
                FILEnn.BCK      Container files

        To generate a C system from the backup tape, you must first copy
        RST.COM to disk, edit it  to  set  correct  disk  and  directory
        designations, then execute it as an indirect command file.  

[[        C Compiler and Library]]                                     Page A-12
        Getting on the Air with Decus C



        After  reading  the kit, install the system using the VBUILD.COM
        command procedure.  One simple way to do this is by  typing  the
        following sequence:  

                $ set default [.command]
                $ @batch vbuild         ! or submit vbuild

        This  builds  a  temporary  batch  control  file  in  your login
        account, submits it to  batch,  and  sends  you  mail  when  the
        process  completes.   Batch.com  requires  some cooperation from
        your login.com file.  

        The compiler, assembler, and run-time library are written to the
        parent  of  [.command]  (generally  [decusc]).   The  tools  are
        written to logical BIN:  which should be defined before starting
        the build process.  (Edit vbuild.com if BIN:  is not defined  in
        your login.com file.) 

        [.command]CCHLP.COM  is  a  command file that adds DECUSC.HLP to
        the system (VMS V2.0) help library.  It requires write-access to
        the help library.  It may not be compatible with later help file
        conventions, nor has it been tested on later releases of VMS.  

        Installation  of  VBUILD  on  an unloaded Vax-11/782 running VMS
        V3.0 takes about 90 minutes.  


        A.5.3  Installation on RSX-11M                ____________ __ _______

        There  are  command files of the format M?????.CMD.  They should
        require no editing for RSX-11M V3.2.  Execute them using the "@"
        system  command,  answering  the  questions  as needed.  Several
        routines in the RSX interface library are specific to  the  V3.2
        release  and  will  not  assemble  on  previous  releases (or on
        RSX-11M emulated on RSTS/E).  


        A.5.4  Installation on RT-11                ____________ __ _____

        An  easy way to build an RT-11 system is to first built a RSTS/E
        system.  Then, use ATPK to execute RTKIT.CMD (after editing)  to
        copy files to an RT-11 format disk.  To run the compiler, define
        logical  device  C:   to  refer  to  the  disk  containing   the
        "#include <>" files and libraries and off you go.  

        Command  procedures  of  the  format  T?????.COM are present for
        "native" RT-11.  They are not optimized to minimize disk storage
        usage.  Decus C has been built on 2 RK05 RT11 systems, using one
        RK05 for system and one for source files.  

        Except  for  "RT11.MAC",  "RT11.EIS",  and  "RSX.MAC" (which are
        everywhere  identical),  there  are  no  known  conflicts  among
        compiler and library file names.  However, given the size of the

[[        C Compiler and Library]]                                     Page A-13
        Getting on the Air with Decus C


        C distribution, it would be prudent to use  separate  disks  for
        the various components of the distribution.  

        The  C  system  runs  on  diskette-based  systems,  such  as the
        PDT-150.  (and even on a VT103  with  two  TU58's!)  No  command
        files  are  present  to  build  the  system on diskette systems.
        Instead, you should copy the  necessary  files  to  diskette  as
        follows:  

             o  Build   an   RT-11   system   containing  file  transfer
                utilities, editors, LINK.SAV, and LIBR.SAV.  

             o  Copy  CC.SAV,  AS.SAV,  and  STDIO.H to this disk (there
                will be only a few free  blocks  left).   This  diskette
                will be defined as the C:  logical device.  

             o  Initialize  a  second  diskette  and  copy  CLIB.OBJ and
                SUPORT.OBJ to it.  

        Your  C  programs  should  be created on the second disk.  There
        will be slightly  more  than  300  blocks  free  after  creating
        CLIB.OBJ  and  SUPORT.OBJ.   Note  that, if you omit some of the
        file transfer utilities, CLIB.OBJ and SUPORT.OBJ may  be  stored
        on  the  system  disk,  freeing  the  second diskette for your C
        programs.  

        You  should  attempt  to keep C program files quite short, using
        the linker/librarian to build larger entities.  For example, the
        MAZE.C  program  (in  [6,2])  needs over 200 blocks of temporary
        disk storage for compilation.  This is  unsatisfactory  in  many
        situations.  

        The  C language system has not been tested on HT-11.  Several of
        the library routines use RT-11 Version 3 monitor calls that  are
        not supported on HT-11.  However, it should not be too difficult
        to "fix" the library as needed.  

        While  all  tools  have been compiled using Vax-11 C, only a few
        have been tested in "native C." 

        Note  also that there are a few incompatiblities between Decus C
        and "standard" C,  and  several  incompatibilities  between  the
        Decus run-time library and Unix-style standard libraries.  


        A.5.5  Supporting Decus C                __________ _____ _

        Decus  C  is distributed in source format.  All files are in the
        public-domain.  WIZARD.DOC contains information on compiler data
        formats and library internal information.  

        This  software is made available without any support whatsoever.
        To  support  the  Decus  C  language,  run-time  library,  or  C
        programs,  you  will  need  to understand and modify Macro and C

[[        C Compiler and Library]]                                     Page A-14
        Getting on the Air with Decus C


        source code.  The authors would  appreciate  your  communicating
        bug   reports   (with   fixes!)   and  suggestions.   The  Decus
        "Structured Languages Special Interest  Group"  is  the  primary
        focus for communication among users of Decus C.  


[[        C Compiler and Library]]                                     Page A-15
        Getting on the Air with Decus C















                                   APPENDIX B

                                  LIBRARY INDEX



        The  following  is  a  keyword  in context index to the standard
        library.  The entry in the left-hand column is the title of  the
        routine in the main library documentation.  


        toascii                     Convert to 7-bit Ascii
        isascii                       Test for 7-bit Ascii
        abort           trap                   Abort program with a BPT
        abs                                    Absolute value
        fabs                          Floating absolute value
        qset            queue                  Add entries to the RT11
        $$fadd                  Floating-point add and subtract
        profile             Print profile data after exit
        rtemt               Execute a RT11 EMT after loading r0
        $$cl16                           Close all I/O channels
        $$flun                                 Allocate a logical unit
        malloc                                 Allocate and free memory
        calloc          memory                 Allocate and initialize
        alloc                                  Allocate memory
        $$abuf          buffers                Allocate memory for i/o
        $$falo          subroutines            Allocate memory for i/o
        sbrk            operating system       Allocate memory from
        isalloc            a pointer points to allocated memory Check if
        $$mchk                   Verify memory allocation pointers
        isalpha                       Test for alphabetic argument
        islower            Test for lower-case alphabetic argument
        isupper            Test for upper-case alphabetic argument
        isalnum                       Test for alphanumeric argument
        strcat                   a string onto another       Concatenate
        strncat                  a string onto another, with Concatenate
        strncpy             Copy one string to another, with count
        $$ltoa                  long to Ascii (any radix)        Convert
        $$fopt             fopen/fwild options argument             Scan
        isalpha            Test for alphabetic argument
        isalnum          Test for alphanumeric argument
        iscntrl          for control character argument             Test
        isdigit                 Test for digit argument
        isgraph               Test for graphic argument
        islower          lower-case alphabetic argument         Test for
        isprint             Test for printable argument

        C Compiler and Library                                          Page B-2
        Library Index


        ispunct           Test for punctuation argument
        isupper          upper-case alphabetic argument         Test for
        isspace            Test for whitespace argument
        $$fcsi                 Parse file name argument for fopen/fwild
        $$fpar          (RMS-11Parse file name argument for fopen/fwild
        $$dtoa               floating point to ASCII             Convert
        ddtoa                floating point to ASCII -- dummy    Convert
        atofd           -- dummy       Convert ASCII to floating point
        $$ctim                $$rtim buffer to Ascii             Convert
        $$c5ta             Convert Radix-50 to Ascii
        r50toa             Convert Radix-50 to Ascii
        fgetname          Convert file name to Ascii
        itoa                Convert integer to Ascii
        itoax                   to hexadecimal Ascii     Convert integer
        itoa8                 integer to octal Ascii             Convert
        toascii               Convert to 7-bit Ascii
        isascii                 Test for 7-bit Ascii
        $$ltoa                 Convert long to Ascii (any radix)
        atoi8           integer        Convert Ascii octal number to
        ascr50                         Convert Ascii to Radix-50
        atod                           Convert Ascii to floating point
        atof                           Convert Ascii to floating point
        ctime            Convert time value to ascii
        ctime                   time buffer to ascii     asctime Convert
        ctime           buffer to ascii        asctime Convert time
        peek                              Peek at a location in RSTS/E
        ftime             Compute time of day (augmented)
        ungetc                            Push back onto an input file
        $$clfu               Flush last record before closing file
        getw            file           Input a binary integer from a
        putw                          Output a binary integer to a file
        fget                           Input a binary record
        fput                          Output a binary record
        msize             Get size of a memory block
        zero                           Clear a block of memory
        fill            character       Fill a block of memory with a
        abort             Abort program with a BPT trap
        localtime            Build time of day buffer
        swabb                  Swap bytes in a buffer
        $$ctim                  Convert $$rtim buffer to Ascii
        $$utim                  Convert $$rtim buffer to Unix time
        ctime             asctime Convert time buffer to ascii
        $$abuf                  memory for i/o buffers          Allocate
        $$flsh                    Flush output buffers
        fflush                    Flush output buffers
        localtime                              Build time of day buffer
        swabi                                  Byte swap an integer
        copy                 a given number of bytes                Copy
        swabb                             Swap bytes in a buffer
        call                   subroutine from C          Call (Fortran)
        callc                  subroutine from C          Call (Fortran)
        $$main          variables              C library global
        $$main                                 C main program
        csv$            environment            C program execution

        C Compiler and Library                                          Page B-3
        Library Index


        $$init                                 C program initialization
        error                  Error exit from C programs
        exit                  Normal exit from C programs
        csv$            restore                C register save and
        call            subroutine from C      Call (Fortran)
        callc           subroutine from C      Call (Fortran)
        $$qiow          service                Call RSX executive
        wrapup                   Dummy routine called on exit
        caller                name of profiled caller             Return
        calltr               Trace path to the caller
        brk             pointer                Change top of memory
        $$cl16                   Close all I/O channels
        ctype           type table             Character classification
        fill                  of memory with a character    Fill a block
        iscntrl               Test for control character argument
        getchar                        Get one character from a file
        index              first instance of a character in a stFind the
        strchr             first instance of a character in a stFind the
        inchr              Find the index of a character in a string
        rindex              last instance of a character in a stFind the
        strrchr             last instance of a character in a stFind the
        putc                        Output one character to a file
        $$putc          (internal)  Output one character to a file
        $$getc                             Get characters (internal)
        isalloc         points to allocated memoryck if a pointer
        ctype           table        Character classification type
        zero                                   Clear a block of memory
        clearerr        flags                  Clear open file's error
        fclear          flags                  Clear open file's error
        $$main                       $$tick -- Clock interrupt rate
        $$cl16                                 Close all I/O channels
        fclose                                 Close an open file
        $$clfu              last record before closing file        Flush
        exit             $$exst -- Exit status code
        exit                  Exit with status code
        iov                          I/O error codes
        $$gcmd                           Parse command line
        msg                   a message on the command terminal    Print
        strcmp                                 Compare strings
        strncmp         count                  Compare strings, with
        $$ctim                                 Compute day of week
        strlen          string                 Compute length of a
        time                                   Compute time of day
        tod                                    Compute time of day
        ftime           (augmented)            Compute time of day
        strcat          onto another           Concatenate a string
        strncat         onto another, with countoncatenate a string
        concat                                 Concatenate strings
        envsave           and restore function context              Save
        iscntrl         argument      Test for control character
        gettty                             Get control terminal name
        setcc           mode only)        Trap Control/C (RSTS/E RT11
        fprintf                      Formatted Conversion
        sprintf                      Formatted Conversion

        C Compiler and Library                                          Page B-4
        Library Index


        $$tens          floating point         Conversion table for
        $$rtim                   Date and time conversion
        $$scan                 Formatted input conversion
        fscanf                 Formatted input conversion
        scanf                  Formatted input conversion
        sscanf                 Formatted input conversion
        $$ctim          Ascii                  Convert $$rtim buffer to
        $$utim          Unix time              Convert $$rtim buffer to
        atofd           floating point -- dummyConvert ASCII to
        atoi8           number to integer      Convert Ascii octal
        ascr50          Radix-50               Convert Ascii to
        atod            floating point         Convert Ascii to
        atof            floating point         Convert Ascii to
        $$c5ta          Ascii                  Convert Radix-50 to
        r50toa          Ascii                  Convert Radix-50 to
        fgetname        Ascii                  Convert file name to
        $$dtoa          to ASCII               Convert floating point
        ddtoa           to ASCII -- dummy      Convert floating point
        itoa                                   Convert integer to Ascii
        itoax           hexadecimal Ascii      Convert integer to
        itoa8           Ascii                  Convert integer to octal
        $$ltoa          (any radix)            Convert long to Ascii
        toupper         upper-case             Convert lower-case to
        atoi            integer                Convert string to
        atol                                   Convert string to long
        ctime           ascii          asctime Convert time buffer to
        ctime           ascii                  Convert time value to
        toascii                                Convert to 7-bit Ascii
        tolower         lower-case             Convert upper-case to
        copy            bytes                  Copy a given number of
        strcpy                                 Copy a string
        strncpy         another, with count    Copy one string to
        cpystr                          String copy
        strncmp          Compare strings, with count
        strncat             onto another, with countConcatenate a string
        strncpy               to another, with count     Copy one string
        strneq           string equality, with count                Test
        $$main                 $$scca -- RT-11 Ctrl/C flag
        profile                  Print profile data after exit
        $$rtim                                 Date and time conversion
        time                   Compute time of day
        tod                    Compute time of day
        ftime                  Compute time of day (augmented)
        localtime                Build time of day buffer
        $$ctim                         Compute day of week
        $$main                $$uic -- RSX-11M default UIC
        $$narg                   Define $$narg default for RT11 startup
        fspool                   Spool file to default print queue
        $$narg          for RT11 startup       Define $$narg default
        iov                         I/O vector definition
        sleep           of seconds             Delay job a given number
        delete                                 Delete a named file
        fmkdl                    Mark file for deletion
        kbinr           read without waiting   Delimiter-free terminal

        C Compiler and Library                                          Page B-5
        Library Index


        kbin              the terminal without delimiters      Read from
        isxdigit          Test for hexadecimal digit
        isdigit                       Test for digit argument
        div$li                            Long division and modulus
        $$div2                        Unsigned division and modulus
        wrapup          exit                   Dummy routine called on
        atofd             to floating point -- dummy       Convert ASCII
        ddtoa                point to ASCII -- dummy    Convert floating
        memdmp                                 Dump memory or registers
        eis$i                                  EIS emulator
        rstsys                  Execute a RSTS EMT
        rtemt                   Execute a RT11 EMT after loading r0
        $$main            $$vms -- Test if VMS emulation
        eis$i                              EIS emulator
        feof                          Test for end of file
        $$main                 $$stnd -- Stack end point
        qset            queue              Add entries to the RT11
        profile              $$prnl -- Profile entry per line
        csv$               C program execution environment
        streq                 Test strings for equality
        strneq                     Test string equality, with count
        error           programs               Error exit from C
        ferr                     Test for file error
        ferror                   Test for file error
        iov                                I/O error codes
        clearerr             Clear open file's error flags
        fclear               Clear open file's error flags
        perror                   Print library error message
        iov                     $$ferr -- File error value
        rstsys                                 Execute a RSTS EMT
        rtemt           loading r0             Execute a RT11 EMT after
        unwind                                 Execute non-local goto
        setjmp                      longjmp -- execute non-local goto
        csv$                         C program execution environment
        $$qiow                        Call RSX executive service
        exit                         $$exst -- Exit status code
        exit                                   Exit with status code
        wrapup               routine called on exit                Dummy
        profile             profile data after exit                Print
        error                            Error exit from C programs
        exit                            Normal exit from C programs
        exit                                 $$exst -- Exit status code
        iov                                  $$ferr -- File error value
        iov                          $$ferr -- File error value
        profile              -- Profile output file               $$pfil
        fclose                   Close an open file
        delete                  Delete a named file
        $$clfu           record before closing file           Flush last
        getchar           one character from a file                  Get
        getw             binary integer from a file              Input a
        fopen                 Open or reopen a file
        putw             a binary integer to a file               Output
        puts              Output a string to a file
        putc                one character to a file               Output

        C Compiler and Library                                          Page B-6
        Library Index


        ungetc              back onto an input file                 Push
        fgets             Read a string from a file
        feof                   Test for end of file
        frec                if record-oriented file                 Test
        $$putc              one character to a file (internal)    Output
        ferr                          Test for file error
        ferror                        Test for file error
        fmkdl                             Mark file for deletion
        rewind                        Rewind a file for re-reading
        ftty                         Test if a file is a terminal
        isatty                       Test if a file is a terminal
        $$fcsi          fopen/fwild      Parse file name argument for
        $$fpar          fopen/fwild (RMS-Parse file name argument for
        fgetname                       Convert file name to Ascii
        $$fopa                Open or reopen a file on RT11
        fwild                        Wild-card file open
        fseek                       Reposition file pointer (seek)
        ftell           subsequent seek    Get file position for
        fspool          queue            Spool file to default print
        clearerr                    Clear open file's error flags
        fclear                      Clear open file's error flags
        fill            with a character       Fill a block of memory
        maxmin          numbers                Find maximum of two
        maxmin          unsigned numbers       Find maximum of two
        maxmin          numbers                Find minimum of two
        maxmin          unsigned numbers       Find minimum of two
        index           of a character in a stringd the first instance
        strchr          of a character in a stringd the first instance
        inchr           character in a string  Find the index of a
        rindex          of a character in a stringd the last instance
        strrchr         of a character in a stringd the last instance
        index           character in aFind the first instance of a
        strchr          character in aFind the first instance of a
        $$main                 -- RT-11 Ctrl/C flag               $$scca
        clearerr             open file's error flags               Clear
        fclear               open file's error flags               Clear
        iov                I/O system internal flags and vectors
        fabs                                   Floating absolute value
        $$tens            Conversion table for floating point
        atod                  Convert Ascii to floating point
        atof                  Convert Ascii to floating point
        atofd                 Convert ASCII to floating point -- dummy
        fps             (FPS)              Set floating point status
        $$dtoa                         Convert floating point to ASCII
        ddtoa           -- dummy       Convert floating point to ASCII
        $$fadd          subtract               Floating-point add and
        $$fmul          multiply/divide        Floating-point
        $$fsav          routines               Floating-point support
        $$clfu          closing file           Flush last record before
        $$flsh                                 Flush output buffers
        fflush                                 Flush output buffers
        $$fcsi               name argument for fopen/fwild    Parse file
        $$fpar               name argument for fopen/fwild (RMParse file
        $$fopt          argument          Scan fopen/fwild options

        C Compiler and Library                                          Page B-7
        Library Index


        fprintf                                Formatted Conversion
        sprintf                                Formatted Conversion
        $$scan          conversion             Formatted input
        fscanf          conversion             Formatted input
        scanf           conversion             Formatted input
        sscanf          conversion             Formatted input
        $$prnt                                 Formatted output
        printf                                 Formatted output
        call            C                Call (Fortran) subroutine from
        callc           C                Call (Fortran) subroutine from
        fps                      point status (FPS)         Set floating
        malloc                    Allocate and free memory
        envsave               Save and restore function context
        envsave                    Multi-level function return
        irand                    Random number generator
        rand                     Random number generator
        $$get                                  Get a record (internal)
        $$getc          (internal)             Get characters
        gettty          name                   Get control terminal
        ftell           subsequent seek        Get file position for
        fileno                                 Get logical unit number
        flun                                   Get logical unit number
        getchar         file                   Get one character from a
        msize           block                  Get size of a memory
        $$gsa                              RMS Get-space routine
        copy                            Copy a given number of bytes
        sleep                      Delay job a given number of seconds
        $$main                       C library global variables
        unwind               Execute non-local goto
        setjmp            -- execute non-local goto              longjmp
        isgraph                       Test for graphic argument
        traps            Operating system trap handlers
        itoax               Convert integer to hexadecimal Ascii
        isxdigit                      Test for hexadecimal digit
        $$cl16                       Close all I/O channels
        iov                                    I/O error codes
        screen                          Screen I/O primitives
        iov             flags and vectors      I/O system internal
        iov                                    I/O vector definition
        $$abuf             Allocate memory for i/o buffers
        $$falo             Allocate memory for i/o subroutines
        $$main             -- Operating system id.                $$opsy
        $$main                   $$pos -- Test if P/OS (Professional)
        $$main                  $$rsts -- Test if RSTS/E
        $$main                   $$vms -- Test if VMS emulation
        ftty                              Test if a file is a terminal
        isatty                            Test if a file is a terminal
        isalloc         allocated memory Check if a pointer points to
        frec                              Test if record-oriented file
        wdleng                         Machine independent sizeof(int)
        inchr           a string      Find the index of a character in
        $$init                       C program initialization
        calloc                    Allocate and initialize memory
        getw            from a file            Input a binary integer

        C Compiler and Library                                          Page B-8
        Library Index


        fget                                   Input a binary record
        fread                                  Input a record
        $$scan                       Formatted input conversion
        fscanf                       Formatted input conversion
        scanf                        Formatted input conversion
        sscanf                       Formatted input conversion
        ungetc               Push back onto an input file
        index           in a strFind the first instance of a character
        strchr          in a strFind the first instance of a character
        rindex          in a striFind the last instance of a character
        strrchr         in a striFind the last instance of a character
        swabi                     Byte swap an integer
        atoi8            Ascii octal number to integer           Convert
        atoi                 Convert string to integer
        asl$li                   Shift long by integer
        asr$u                shift unsigned by integer             right
        getw                    Input a binary integer from a file
        itoa                           Convert integer to Ascii
        putw                   Output a binary integer to a file
        itoax           Ascii          Convert integer to hexadecimal
        itoa8                          Convert integer to octal Ascii
        iov             vectors     I/O system internal flags and
        $$get                    Get a record (internal)
        $$getc                 Get characters (internal)
        $$putc            character to a file (internal)      Output one
        $$main                 $$tick -- Clock interrupt rate
        ftty                    Test if a file is a terminal
        isatty                  Test if a file is a terminal
        sleep           seconds          Delay job a given number of
        rindex          character in aFind the last instance of a
        strrchr         character in aFind the last instance of a
        $$clfu          closing file     Flush last record before
        strlen                         Compute length of a string
        perror                           Print library error message
        $$main                               C library global variables
        profile           -- Profile entry per line               $$prnl
        $$gcmd                   Parse command line
        gets                            Read a line from stdin
        $$link                    Print memory list
        rtemt                 a RT11 EMT after loading r0        Execute
        peek                         Peek at a location in RSTS/E
        $$put                          Write a logical record
        $$flun                      Allocate a logical unit
        fileno                             Get logical unit number
        flun                               Get logical unit number
        div$li          modulus                Long division and
        atol                 Convert string to long
        mul$l                 Multiply long by long
        asl$l                    shift long by long
        asl$li                           Shift long by integer
        mul$l                         Multiply long by long
        asl$l                            shift long by long
        $$ltoa          radix)         Convert long to Ascii (any
        setjmp               -- save state for longjmp            setjmp

        C Compiler and Library                                          Page B-9
        Library Index


        setjmp          non-local goto         longjmp -- execute
        tolower          Convert upper-case to lower-case
        islower         argument      Test for lower-case alphabetic
        toupper                        Convert lower-case to upper-case
        wdleng          sizeof(int)            Machine independent
        $$main                               C main program
        fmkdl                                  Mark file for deletion
        maxmin                            Find maximum of two numbers
        maxmin          numbers           Find maximum of two unsigned
        alloc                         Allocate memory
        malloc               Allocate and free memory
        calloc                  and initialize memory           Allocate
        isalloc            points to allocated memory Check if a pointer
        zero                  Clear a block of memory
        realloc                     Reallocate memory
        $$mchk          pointers        Verify memory allocation
        msize                    Get size of a memory block
        $$abuf                        Allocate memory for i/o buffers
        $$falo          subroutines   Allocate memory for i/o
        sbrk            system        Allocate memory from operating
        $$link                           Print memory list
        memdmp                            Dump memory or registers
        brk                      Change top of memory pointer
        fill                   Fill a block of memory with a character
        perror             Print library error message
        msg             terminal       Print a message on the command
        maxmin                            Find minimum of two numbers
        maxmin          numbers           Find minimum of two unsigned
        setcc                     (RSTS/E RT11 mode only) Trap Control/C
        trace                  Profile support module (with trace)
        div$li               Long division and modulus
        $$div2           Unsigned division and modulus
        envsave         return                 Multi-level function
        mul$l                                  Multiply long by long
        $$fmul                  Floating-point multiply/divide
        $$main                 -- RSX-11M task name               $$task
        gettty            Get control terminal name
        $$fcsi          fopen/fwild Parse file name argument for
        $$fpar          fopen/fwild Parse file name argument for
        caller                          Return name of profiled caller
        fgetname                  Convert file name to Ascii
        delete                        Delete a named file
        $$narg          startup       Define $$narg default for RT11
        unwind                         Execute non-local goto
        setjmp              longjmp -- execute non-local goto
        exit            programs               Normal exit from C
        $$prmt                                 Null prompt pointer
        fileno                Get logical unit number
        flun                  Get logical unit number
        irand                           Random number generator
        rand                            Random number generator
        copy                      Copy a given number of bytes
        sleep                Delay job a given number of seconds
        atoi8              Convert Ascii octal number to integer

        C Compiler and Library                                         Page B-10
        Library Index


        maxmin             Find maximum of two numbers
        maxmin                 of two unsigned numbers      Find maximum
        maxmin             Find minimum of two numbers
        maxmin                 of two unsigned numbers      Find minimum
        itoa8               Convert integer to octal Ascii
        atoi8                    Convert Ascii octal number to integer
        getchar         file               Get one character from a
        putc                            Output one character to a file
        $$putc          (internal)      Output one character to a file
        strncpy         with count        Copy one string to another,
        setcc                (RSTS/E RT11 mode only)      Trap Control/C
        ungetc                       Push back onto an input file
        strcat            Concatenate a string onto another
        strncat           Concatenate a string onto another, with count
        fopen                                  Open or reopen a file
        $$fopa          RT11                   Open or reopen a file on
        fwild                   Wild-card file open
        fclose                        Close an open file
        clearerr                         Clear open file's error flags
        fclear                           Clear open file's error flags
        $$main                       $$opsy -- Operating system id.
        traps           handlers               Operating system trap
        sbrk              Allocate memory from operating system
        $$main          variables              Operating-system unique
        $$main          id.                  $$opsy -- Operating system
        $$fopt                Scan fopen/fwild options argument
        memdmp                     Dump memory or registers
        fopen                             Open or reopen a file
        $$fopa                            Open or reopen a file on RT11
        putw            to a file              Output a binary integer
        fput                                   Output a binary record
        fwrite                                 Output a record
        puts            file                   Output a string to a
        putc            a file                 Output one character to
        $$putc          a file (internal)      Output one character to
        $$prnt                       Formatted output
        printf                       Formatted output
        $$flsh                           Flush output buffers
        fflush                           Flush output buffers
        profile              $$pfil -- Profile output file
        $$main                $$pos -- Test if P/OS (Professional)
        $$gcmd                                 Parse command line
        $$fcsi          for fopen/fwild        Parse file name argument
        $$fpar          for fopen/fwild (RMS-11)arse file name argument
        calltr                           Trace path to the caller
        peek            RSTS/E                 Peek at a location in
        profile               -- Profile entry per line           $$prnl
        profile         file                 $$pfil -- Profile output
        $$main             $$stnd -- Stack end point
        $$tens              table for floating point          Conversion
        atod                 Ascii to floating point             Convert
        atof                 Ascii to floating point             Convert
        atofd                ASCII to floating point -- dummy    Convert
        fps                       Set floating point status (FPS)

        C Compiler and Library                                         Page B-11
        Library Index


        $$dtoa                Convert floating point to ASCII
        ddtoa                 Convert floating point to ASCII -- dummy
        brk               Change top of memory pointer
        $$prmt                     Null prompt pointer
        fseek                  Reposition file pointer (seek)
        isalloc         allocated meCheck if a pointer points to
        $$mchk               memory allocation pointers           Verify
        isalloc         memoCheck if a pointer points to allocated
        $$main          (Professional)       $$pos -- Test if P/OS
        ftell           seek          Get file position for subsequent
        screen                      Screen I/O primitives
        msg             command terminal       Print a message on the
        perror          message                Print library error
        $$link                                 Print memory list
        profile         exit                   Print profile data after
        fspool           Spool file to default print queue
        isprint                       Test for printable argument
        profile         per line             $$prnl -- Profile entry
        $$main                -- Test if P/OS (Professional)       $$pos
        profile                      $$prnl -- Profile entry per line
        profile                      $$pfil -- Profile output file
        trace           (with trace)           Profile support module
        profile                          Print profile data after exit
        caller                  Return name of profiled caller
        $$main                          C main program
        csv$            environment          C program execution
        $$init                               C program initialization
        abort                            Abort program with a BPT trap
        error                Error exit from C programs
        exit                Normal exit from C programs
        $$prmt                            Null prompt pointer
        ispunct                       Test for punctuation argument
        ungetc          file                   Push back onto an input
        qset               entries to the RT11 queue                 Add
        fspool           file to default print queue               Spool
        rtemt                EMT after loading r0         Execute a RT11
        $$svr1                  Save registers r1-r5 on the stack
        $$ltoa              long to Ascii (any radix)            Convert
        ascr50                Convert Ascii to Radix-50
        $$c5ta                         Convert Radix-50 to Ascii
        r50toa                         Convert Radix-50 to Ascii
        irand                                  Random number generator
        rand                                   Random number generator
        $$main              -- Clock interrupt rate               $$tick
        rewind               Rewind a file for re-reading
        gets                                   Read a line from stdin
        fgets           file                   Read a string from a
        kbin            without delimiters     Read from the terminal
        kbinr                         terminal read withouDelimiter-free
        realloc                                Reallocate memory
        fread                          Input a record
        fget                    Input a binary record
        fwrite                        Output a record
        fput                   Output a binary record

        C Compiler and Library                                         Page B-12
        Library Index


        $$put                  Write a logical record
        $$get                            Get a record (internal)
        $$clfu          file        Flush last record before closing
        frec                           Test if record-oriented file
        csv$            restore              C register save and
        memdmp                  Dump memory or registers
        $$svr1          stack             Save registers r1-r5 on the
        fopen                          Open or reopen a file
        $$fopa                         Open or reopen a file on RT11
        fseek           (seek)                 Reposition file pointer
        csv$               C register save and restore
        envsave                       Save and restore function context
        caller          caller                 Return name of profiled
        envsave           Multi-level function return
        rewind          re-reading             Rewind a file for
        asr$u           integer                right shift unsigned by
        $$gsa                                  RMS Get-space routine
        $$fpar                for fopen/fwild (RParse file name argument
        $$gsa                    RMS Get-space routine
        wrapup                           Dummy routine called on exit
        $$fsav                         support routines   Floating-point
        rstsys                       Execute a RSTS EMT
        $$main                               $$rsts -- Test if RSTS/E
        $$main               $$rsts -- Test if RSTS/E
        peek             Peek at a location in RSTS/E
        setcc                  Trap Control/C (RSTS/E RT11 mode only)
        $$qiow                            Call RSX executive service
        $$main                        $$uic -- RSX-11M default UIC
        $$main                       $$task -- RSX-11M task name
        $$main                       $$scca -- RT-11 Ctrl/C flag
        $$fopa             or reopen a file on RT11                 Open
        rtemt           r0           Execute a RT11 EMT after loading
        setcc                Control/C (RSTS/E RT11 mode only)      Trap
        qset                Add entries to the RT11 queue
        $$narg              $$narg default for RT11 startup       Define
        $$ctim                       Convert $$rtim buffer to Ascii
        $$utim                       Convert $$rtim buffer to Unix time
        envsave         function context       Save and restore
        $$svr1          the stack              Save registers r1-r5 on
        csv$                        C register save and restore
        setjmp                       setjmp -- save state for longjmp
        $$fopt          argument               Scan fopen/fwild options
        $$main          flag                 $$scca -- RT-11 Ctrl/C
        screen                                 Screen I/O primitives
        sleep            job a given number of seconds             Delay
        ftell                   for subsequent seek    Get file position
        fseek                    file pointer (seek)          Reposition
        $$qiow              Call RSX executive service
        fps             status (FPS)           Set floating point
        setjmp          longjmp                setjmp -- save state for
        asl$li                                 Shift long by integer
        asl$l                                  shift long by long
        asr$u           integer          right shift unsigned by
        msize                              Get size of a memory block

        C Compiler and Library                                         Page B-13
        Library Index


        wdleng             Machine independent sizeof(int)
        fspool          print queue            Spool file to default
        $$main                       $$stnd -- Stack end point
        $$svr1                    r1-r5 on the stack      Save registers
        $$narg                default for RT11 startup     Define $$narg
        setjmp                  setjmp -- save state for longjmp
        fps                 Set floating point status (FPS)
        exit                    $$exst -- Exit status code
        exit                         Exit with status code
        gets                  Read a line from stdin
        $$main                               $$stnd -- Stack end point
        cpystr                                 String copy
        strlen             Compute length of a string
        strcpy                          Copy a string
        index              of a character in a stFind the first instance
        strchr             of a character in a stFind the first instance
        inchr              of a character in a string     Find the index
        rindex             of a character in a strFind the last instance
        strrchr            of a character in a strFind the last instance
        strneq          count             Test string equality, with
        fgets                           Read a string from a file
        strcat                   Concatenate a string onto another
        strncat         with counConcatenate a string onto another,
        puts                          Output a string to a file
        strncpy         count         Copy one string to another, with
        atoi                           Convert string to integer
        atol                           Convert string to long
        strcmp                         Compare strings
        concat                     Concatenate strings
        streq                             Test strings for equality
        strncmp                        Compare strings, with count
        call                    Call (Fortran) subroutine from C
        callc                   Call (Fortran) subroutine from C
        $$falo                  memory for i/o subroutines      Allocate
        ftell            Get file position for subsequent seek
        $$fadd                         add and subtract   Floating-point
        trace           trace)         Profile support module (with
        $$fsav                  Floating-point support routines
        swabb                                  Swap bytes in a buffer
        swabi                             Byte swap an integer
        sbrk             memory from operating system           Allocate
        $$main             $$opsy -- Operating system id.
        iov             and vectors        I/O system internal flags
        traps                        Operating system trap handlers
        ctype              classification type table           Character
        $$tens                      Conversion table for floating point
        $$main          name                 $$task -- RSX-11M task
        $$main               $$task -- RSX-11M task name
        msg                     on the command terminal  Print a message
        ftty               Test if a file is a terminal
        isatty             Test if a file is a terminal
        gettty                     Get control terminal name
        kbinr           waiting Delimiter-free terminal read without
        kbin            delimiterRead from the terminal without

        C Compiler and Library                                         Page B-14
        Library Index


        isascii                                Test for 7-bit Ascii
        isalpha         argument               Test for alphabetic
        isalnum         argument               Test for alphanumeric
        iscntrl         character argument     Test for control
        isdigit                                Test for digit argument
        feof                                   Test for end of file
        ferr                                   Test for file error
        ferror                                 Test for file error
        isgraph         argument               Test for graphic
        isxdigit        digit                  Test for hexadecimal
        islower         alphabetic argument    Test for lower-case
        isprint         argument               Test for printable
        ispunct         argument               Test for punctuation
        isupper         alphabetic argument    Test for upper-case
        isspace         argument               Test for whitespace
        $$main          (Professional)$$pos -- Test if P/OS
        $$main                       $$rsts -- Test if RSTS/E
        $$main                        $$vms -- Test if VMS emulation
        ftty            terminal               Test if a file is a
        isatty          terminal               Test if a file is a
        frec            file                   Test if record-oriented
        strneq          with count             Test string equality,
        streq           equality               Test strings for
        $$main          rate                 $$tick -- Clock interrupt
        $$utim           $$rtim buffer to Unix time              Convert
        ctime                  asctime Convert time buffer to ascii
        $$rtim                        Date and time conversion
        time                           Compute time of day
        tod                            Compute time of day
        ftime                          Compute time of day (augmented)
        localtime                        Build time of day buffer
        ctime                          Convert time value to ascii
        brk                             Change top of memory pointer
        calltr                                 Trace path to the caller
        trace             support module (with trace)            Profile
        setcc           RT11 mode only)        Trap Control/C (RSTS/E
        abort               program with a BPT trap                Abort
        traps                 Operating system trap handlers
        maxmin                 Find maximum of two numbers
        maxmin                 Find minimum of two numbers
        maxmin                 Find maximum of two unsigned numbers
        maxmin                 Find minimum of two unsigned numbers
        ctype                   classification type table      Character
        $$main              -- RSX-11M default UIC                 $$uic
        $$main          UIC                  $$uic -- RSX-11M default
        $$main                Operating-system unique variables
        $$flun              Allocate a logical unit
        fileno                     Get logical unit number
        flun                       Get logical unit number
        $$utim                $$rtim buffer to Unix time         Convert
        $$div2          modulus                Unsigned division and
        asr$u                      right shift unsigned by integer
        maxmin             Find maximum of two unsigned numbers
        maxmin             Find minimum of two unsigned numbers

        C Compiler and Library                                         Page B-15
        Library Index


        toupper          Convert lower-case to upper-case
        isupper         argument      Test for upper-case alphabetic
        tolower                        Convert upper-case to lower-case
        iov               $$ferr -- File error value
        abs                           Absolute value
        fabs                 Floating absolute value
        ctime                     Convert time value to ascii
        $$main                C library global variables
        $$main                          unique variablesOperating-system
        iov                                I/O vector definition
        iov                 internal flags and vectors        I/O system
        $$mchk          pointers               Verify memory allocation
        $$main                $$vms -- Test if VMS emulation
        $$main          emulation            $$vms -- Test if VMS
        kbinr            terminal read without waiting    Delimiter-free
        $$ctim                  Compute day of week
        isspace                       Test for whitespace argument
        kbin                 from the terminal without delimiters   Read
        kbinr                    terminal read without waiDelimiter-free
        $$put                                  Write a logical record