UU      UU      CCCCCC      LL                      
                UU      UU      CCCCCC      LL                      
                UU      UU    CC      CC    LL                ++    
                UU      UU    CC      CC    LL                ++    
                UU      UU    CC            LL                ++    
                UU      UU    CC            LL                ++    
                UU      UU    CC            LL            ++++++++++
                UU      UU    CC            LL            ++++++++++
                UU      UU    CC            LL                ++    
                UU      UU    CC            LL                ++    
                UU      UU    CC      CC    LL                ++    
                UU      UU    CC      CC    LL                ++    
                  UUUUUU        CCCCCC      LLLLLLLLLL              
                  UUUUUU        CCCCCC      LLLLLLLLLL              







                              USER COMMAND LINKAGE-plus

                                       V08.02a

                                     04 Apr 1991


                                For RT-11 V5.0 - V5.6
                                 TSX-Plus V4.1 - V6.5
                                      and RTEM





                                  William K. Walker

                                  RDB/Alpha Systems
                                    P. O. Box 149
                                Alpha, OH  45301-0149
                                 (513) 426-0344/7094
                                rdbalpha@mcimail.com





                       SPECIAL NOTE TO SCIENTISTS/RESEARCHERS

                                  Read the manual!

                                                                    Page ii



                             TABLE OF CONTENTS



        1.0  ACKNOWLEDGEMENTS . . . . . . . . . . . . . . . . . . . . . . 1

        2.0  IMPORTANT NOTICES  . . . . . . . . . . . . . . . . . . . . . 2

        3.0  BEFORE YOU GET STARTED . . . . . . . . . . . . . . . . . . . 3

        4.0  ABOUT THIS DOCUMENT  . . . . . . . . . . . . . . . . . . . . 4

        5.0  INTRODUCTION . . . . . . . . . . . . . . . . . . . . . . . . 5
        5.1  UCL+ Differences . . . . . . . . . . . . . . . . . . . . . . 5
        5.2  UCL+ Enhancements  . . . . . . . . . . . . . . . . . . . . . 6

        6.0  INSTALLATION . . . . . . . . . . . . . . . . . . . . . . . . 8
        6.1  Installing UCL.SAV . . . . . . . . . . . . . . . . . . . .  10
        6.1.1  Installing UCL.SAV On RT-11 Systems  . . . . . . . . . .  10
        6.1.1.1  Installation As A UCL (UCL.SAV => UCL.SAV) . . . . . .  10
        6.1.1.2  Installation As A UCF (UCL.SAV => UCF.SAV) . . . . . .  11
        6.1.2  Installing UCL.SAV On TSX-Plus Systems . . . . . . . . .  11
        6.1.2.1  Installation As A UCL (UCL.SAV => TSXUCL.SAV)  . . . .  12
        6.1.2.2  Installation As A UCI (UCL.SAV => UKMON.SAV) . . . . .  12
        6.2  Installing UCLXM.SAV . . . . . . . . . . . . . . . . . . .  13
        6.2.1  Installing UCLXM.SAV On RT-11 Systems  . . . . . . . . .  13
        6.2.1.1  Installation As A UCL (UCLXM.SAV => UCL.SAV) . . . . .  14
        6.2.1.2  Installation As A UCF (UCLXM.SAV => UCF.SAV) . . . . .  14
        6.2.2  Installing UCLXM.SAV On TSX-Plus Systems . . . . . . . .  15
        6.2.2.1  Installation As A UCL (UCLXM.SAV => TSXUCL.SAV)  . . .  16
        6.2.2.2  Installation As A UCI (UCLXM.SAV => UKMON.SAV) . . . .  17
        6.3  Installing UCLXD.SAV . . . . . . . . . . . . . . . . . . .  18
        6.3.1  Installing UCLXD.SAV On RT-11 Systems  . . . . . . . . .  18
        6.3.1.1  Installation As A UCL (UCLXD.SAV => UCL.SAV) . . . . .  18
        6.3.1.2  Installation As A UCF (UCLXD.SAV => UCF.SAV) . . . . .  19
        6.3.2  Installing UCLXD.SAV On TSX-Plus Systems . . . . . . . .  20
        6.3.2.1  Installation As A UCL (UCLXD.SAV => TSXUCL.SAV)  . . .  21
        6.3.2.2  Installation As A UCI (UCLXD.SAV => UKMON.SAV) . . . .  22
        6.4  Installing The CI Handler  . . . . . . . . . . . . . . . .  24
        6.5  Installing UCL+ HELP . . . . . . . . . . . . . . . . . . .  25
        6.6  Installing The UCL+ Distribution Under RTEM  . . . . . . .  26

        7.0  HOW IT WORKS . . . . . . . . . . . . . . . . . . . . . . .  27
        7.1  RT-11 Command Processing With UCL Support  . . . . . . . .  27
        7.2  RT-11 Command Processing With UCF Support  . . . . . . . .  28
        7.3  TSX-Plus Command Processing  . . . . . . . . . . . . . . .  28

        8.0  SYMBOLS  . . . . . . . . . . . . . . . . . . . . . . . . .  30
        8.1  Defining Symbols . . . . . . . . . . . . . . . . . . . . .  30
        8.2  Deleting Symbols . . . . . . . . . . . . . . . . . . . . .  32
        8.3  Entering Special Characters  . . . . . . . . . . . . . . .  32
        8.4  Running UCL+ Directly  . . . . . . . . . . . . . . . . . .  33

                                                                   Page iii



        8.5  Advanced Techniques  . . . . . . . . . . . . . . . . . . .  34
        8.5.1  Using The Quote Character ("|")  . . . . . . . . . . . .  34
        8.5.2  Argument String Parsing ("^n") . . . . . . . . . . . . .  35
        8.5.3  Specifying Default Strings . . . . . . . . . . . . . . .  36

        9.0  "HARD-WIRED" COMMANDS  . . . . . . . . . . . . . . . . . .  39
        9.1  CHAIN Command  . . . . . . . . . . . . . . . . . . . . . .  40
        9.2  DISPLAY Command  . . . . . . . . . . . . . . . . . . . . .  41
        9.3  ERASE Command  . . . . . . . . . . . . . . . . . . . . . .  43
        9.4  LIST Command . . . . . . . . . . . . . . . . . . . . . . .  44
        9.5  PASS_ON Command  . . . . . . . . . . . . . . . . . . . . .  46
        9.6  PATH Command . . . . . . . . . . . . . . . . . . . . . . .  47
        9.7  PROMPT Command . . . . . . . . . . . . . . . . . . . . . .  48
        9.8  RECALL Command . . . . . . . . . . . . . . . . . . . . . .  49
        9.9  RELOAD command . . . . . . . . . . . . . . . . . . . . . .  50
        9.10  STORE Command . . . . . . . . . . . . . . . . . . . . . .  51
        9.11  UCI_MODE Command  . . . . . . . . . . . . . . . . . . . .  52

        10.0  CI HANDLER  . . . . . . . . . . . . . . . . . . . . . . .  53

        11.0  INFORMATIONAL MESSAGES  . . . . . . . . . . . . . . . . .  55

        12.0  ERROR MESSAGES  . . . . . . . . . . . . . . . . . . . . .  57
        12.1  UCL+ "Warning" Messages (?UCL-W-...)  . . . . . . . . . .  58
        12.2  UCL+ Error Messages (?UCL-E-...)  . . . . . . . . . . . .  59
        12.3  UCL+ "Fatal" Messages (?UCL-F-...)  . . . . . . . . . . .  62
        12.4  Global Region Loader Errors (?UCLGRL-F-...) . . . . . . .  64
        12.5  CI Handler Errors (?CI-...) . . . . . . . . . . . . . . .  65

        13.0  EXAMPLES  . . . . . . . . . . . . . . . . . . . . . . . .  66

        14.0  V7 AND V8 RELEASE NOTES . . . . . . . . . . . . . . . . .  67

        15.0  APPLICATION NOTES . . . . . . . . . . . . . . . . . . . .  72
        15.1  Executing Command/Control Files "By-Name" . . . . . . . .  72
        15.2  Sending Escape Sequences To The Printer . . . . . . . . .  72
        15.3  Moving From UCL+ V6x To UCL+ V8.xx  . . . . . . . . . . .  73
        15.4  Disabling Argument Parsing  . . . . . . . . . . . . . . .  74
        15.5  Hints and Kinks: UCF, UCI, And SET UCL FIRST  . . . . . .  75
        15.5.1  Interception Of Monitor Commands  . . . . . . . . . . .  75
        15.5.2  Improper Expansion Of Monitor Commands  . . . . . . . .  75
        15.5.3  Single Key Commands . . . . . . . . . . . . . . . . . .  76
        15.6  UCL+ Assembly Conditionals  . . . . . . . . . . . . . . .  77
        15.7  Changing The RT-11 UCL/UCF Device/File Name . . . . . . .  78
        15.8  Changing The TSX-Plus UCL/UCI Defaults  . . . . . . . . .  80
        15.9  Controlling Command Line Factoring  . . . . . . . . . . .  81
        15.10  Patching UCL+ For RT-11 V5.1 . . . . . . . . . . . . . .  82
        15.11  Implementing The CD And RNO Commands . . . . . . . . . .  83
        15.12  Avoiding Conflicts With The SL RECALL Command  . . . . .  84
        15.13  Avoiding Conflicts With The TSX-Plus PROMPT Command  . .  85
        15.14  Controlling External Data (XD) File Initialization . . .  86
        15.15  Enabling/Disabling UCL+ External Data (XD) Support . . .  88

                                                                    Page iv



        15.16  Changing The External Data (XD) Device/File Name . . . .  89
        15.17  Implementing Both Global And Local Symbols Under
               TSX-Plus . . . . . . . . . . . . . . . . . . . . . . . .  90
        15.18  Eliminating the TSX-Plus UCL Data File (TSXUCL.TSX)  . .  91

        16.0  REPORTING PROBLEMS AND SUGGESTIONS  . . . . . . . . . . .  92

        17.0  WISH LIST . . . . . . . . . . . . . . . . . . . . . . . .  93

        18.0  UCL+ COMMAND AND SYNTAX SUMMARY . . . . . . . . . . . . .  94

        19.0  UCL+ CUSTOMIZATION PATCH SUMMARY  . . . . . . . . . . . .  95

        20.0  INDEX . . . . . . . . . . . . . . . . . . . . . . . . . .  96

          UCL+ -- User Command Linkage Program - V08.02a             Page 1
                  Acknowledgements


          1.0  ACKNOWLEDGEMENTS 

          Throughout  this  document,  reference  is  made to the RT-11 and
          TSX-Plus operating systems.  RT-11 is a product of Digital Equip-
          ment  Corporation,  Maynard,  MA;  TSX-Plus is a product of S & H
          Computer Systems, Nashville, TN.  

          The  "^0" construct and the facility for entering octal character
          codes were added at the suggestion of  C. E. Chew  of  Australia.
          This ended what was, at the time, an unprecedented four months of
          stability for the UCL+ package.  

          The  idea  of  adding a provision for specifying default argument
          strings in symbol definitions  came  from  Rally  Barnard,  Albu-
          querque, NM.  

          The addition of the LIST/INDIVIDUAL facility came about because I
          finally got tired of everybody asking me for it  and  because  it
          is,  after  all,  rather convenient.  The elimination of the dis-
          tinction between XM and non-XM "STORE" files was implemented  for
          basically the same reason.  

          The informational messages (?UCL-I-etc.) were added to keep Rally
          from shooting himself in the foot.  

          Greg Adams provided the final increment of irritation that led to
          the implementation of the "external data" version of UCL+.  

          Tim  Clarke submitted some minor spelling and grammatical correc-
          tions in gentle revenge for my note on the cover page.   He  also
          came  up  with  the  sneaky  TSX-Plus  patch described in section
          15.18.  

          Rally  Barnard  gets the bug-of-the-year award for discovering an
          error that has been lurking in the weeds for four years.  

          The field testing for this version was performed by Billy Youdel-
          man and myself (of course).  

          UCL+ -- User Command Linkage Program - V08.02a             Page 2
                  Important Notices


          2.0  IMPORTANT NOTICES 


                                  RT-11 V5.1 USERS                                  ________________

          IF YOU ARE GOING TO USE THIS VERSION OF UCL+ UNDER AN RT-11  V5.1
          MONITOR (OR EQUIVALENT RTEM-11 MONITOR), YOU MUST APPLY THE PATCH
          IN SECTION 15.10 FOR UCL+ TO WORK PROPERLY (IT'S NOT MY FAULT  --
          IT'S DEC'S FAULT).  

                      RT-11 V5.4C/TSX-PLUS V6.3 OR LATER USERS                      ________________________________________

          SOME  VERSIONS  OF  THE  SINGLE-LINE  EDITOR IMPLEMENT A "RECALL"
          COMMAND AS A SET OPTION.  IF THIS FUNCTIONALITY  IS  ENABLED,  IT
          PREEMPTS  THE  UCL+  RECALL  COMMAND.  SEE THE APPLICATION NOTES,
          SECTION 15.12, FOR A  DISCUSSION  OF  HOW  TO  WORK  AROUND  THIS
          PROBLEM.  

                            V07.54 OR EARLIER UCL+ USERS                            ____________________________

          THE "CD" AND "RNO" COMMANDS ARE NO LONGER INCLUDED IN THE DISTRI-
          BUTED UCL+ PROGRAM.  "CD" CAN NOW BE DEFINED AS A SYMBOL, AS  CAN
          A  BASE-LINE  "RNO"  COMMAND.  SEE THE APPLICATION NOTES, SECTION
          15.11, FOR DETAILS.  THE STANDARD, HARD-WIRED  "RNO"  COMMAND  IS
          ALSO AVAILABLE AS A CONDITIONAL ASSEMBLY (SEE SECTION 15.6).  

                            V07.57 OR EARLIER UCL+ USERS                            ____________________________

          THE  "NOSL"  AND "SLON" COMMANDS HAVE BEEN ELIMINATED.  AN ESCAPE
          CHARACTER CAN NOW BE ENTERED AS ITS OCTAL OR DECIMAL CODE ("<33>"
          OR "<27.>").  

          UCL+ -- User Command Linkage Program - V08.02a             Page 3
                  Before You Get Started


          3.0  BEFORE YOU GET STARTED 

          Before  you  start  using  UCL+,  there are a few things that you
          should keep in mind.  

                o  You  don't  have  to get fancy.  With a couple of fairly
                   minor exceptions, you can just  use  UCL+  as  a  direct
                   replacement  for  your  distributed UCL.  Try the sneaky
                   stuff once you get accustomed to the basic facilities.  

                o  If you intend to use the extended features, particularly
                   UCF or UCI_MODE, make sure you read  the  available  do-
                   cumentation.   Note  that  there are a number of goodies
                   contained in the application notes (section 15.0) at the
                   end of this manual.  

                o  READ  THE  INSTALLATION  INSTRUCTIONS  (section 6.0) for
                   your particular environment.  

                o  RTEM users can assume that the material concerning RT-11
                   also applies to the RTEM  equivalent  environment.   The
                   significant  exceptions  are the installation procedures
                   and the use of the UCF facility.  


          UCL+ -- User Command Linkage Program - V08.02a             Page 4
                  About This Document


          4.0  ABOUT THIS DOCUMENT 

          A fair amount of effort has gone into this manual to give reason-
          ably comprehensive coverage of the contents of the UCL+ distribu-
          tion  kit.   It  does  not,  however, attempt to include material
          already available in the relevant operating system documentation,
          nor is there extensive coverage of internals.  

          Where  examples  are  felt to be necessary, the following conven-
          tions are followed:  

                o  Examples,  unless  otherwise  noted, are for RT-11 V5.0;
                   no "factoring" is used.  

                o  In most examples, operator input is underlined.  When an
                   underscore character ("_") must be used as part  of  the
                   example text, operator input is not underlined.  

                o  All  visible lines of input are assumed to be terminated
                   with a carriage return.  

                o  "Non-printing"  characters  and  control  characters are
                   identified by an abbreviation enclosed by angle brackets
                   ("<>").  E.g., 
                    -  <ret>    = carriage return (CR) 
                    -  <esc>    = escape (ESC) 
                    -  <ctrl/C> = control-C (ETX) 
                    -  <ctrl/Y> = control-Y (EM) 

                   Note,  however, that instances of digits enclosed in an-
                   gle brackets (e.g.,"<003>","<27.>", etc.) are a part  of
                   the normal UCL+ symbol definition syntax.  

                o  Examples and procedure descriptions, except where noted,
                   assume that all  necessary  files  are  on  the  default
                   device (DK:).  


          UCL+ -- User Command Linkage Program - V08.02a             Page 5
                  Introduction


          5.0  INTRODUCTION 

          UCL+  is  a user command linkage program for use with RT-11 V5 or
          later, RTEM V2.0 or later, and TSX-Plus V4.1 or  later  monitors.
          It contains full support for the user command related features of
          these operating systems.  These include:  

                o  UCL - User Command Linkage (RT-11, RTEM, and TSX-Plus) 

                o  UCI - User Command Interface (TSX-Plus, V5.0 or later) 

                o  UCF - User Commands First (RT-11, starting with V5.2) 

          In  general,  UCL+  can  be  used as a direct replacement for the
          "UCLs" distributed with these operating systems.  There are  some
          relatively  minor  incompatibilities between UCL+ and the distri-
          buted versions, as well as a substantial number of  enhancements.
          The remainder of this section summarizes these differences.  


          5.1  UCL+ Differences 

          UCL+  is  upward compatible with the UCL program distributed with
          RT-11 (and the TSX-Plus TSXUCL program) with the following excep-
          tions.  

                o  UCL+  accepts  the  "VMS-like"  symbol definition syntax
                   used by DEC's UCL, but  it  ignores  it.   Instead,  the
                   number  of  characters  that  must be typed to specify a
                   command or symbol unambiguously is a  function  of  con-
                   text.   E.g.,  if  you have defined two symbols starting
                   with "S", "SUPPER"  and  "SUPER",  you  must  type  four
                   characters  to  distinguish  between  them.  However, if
                   they are "SIPPER" and "SUPER", only two  characters  are
                   necessary.  

                o  UCL+  currently  allows symbol names of no more than six
                   characters.  If you use a longer name in  a  definition,
                   UCL+  will  truncate  it  to  six characters and issue a
                   warning message to that effect.  

                o  UCL+  is  different  from the TSX-Plus TSXUCL program in
                   that UCL+ does not "forget" symbol definitions  after  a
                   user logs off.  In addition, if you do not choose to use
                   the "external data" version of UCL+,  all  commands  and
                   symbols  will  be  "global",  rather  than  local  to  a
                   specific user.  


          UCL+ -- User Command Linkage Program - V08.02a             Page 6
                  Introduction


          5.2  UCL+ Enhancements 

          UCL+ contains a number of extensions to the distributed RT-11 and
          TSX-Plus UCL programs.  The following list is a  summary  of  the
          most  important ones.  Refer to the relevant sections of this do-
          cument for further detail.  

                o  UCL+  is  optimized to minimize disk access.  The symbol
                   definitions are contained in internal tables rather than
                   a  separate data file (an "external data" variant is op-
                   tionally available), and an "execute-immediate" mode  is
                   available  for  commands  that  are  defined in terms of
                   other UCL commands.  

                o  More than one symbol definition can be deleted in a sin-
                   gle command line via the  ERASE  command.   All  current
                   symbol definitions can be removed with ERASE *.  

                o  You can chain to additional "UCLs".  

                o  A  "run-by-name  path"  can be defined which extends the
                   monitor's "run-from-SY:" default.  

                o  You  can  STORE/RECALL  the  program  settings to/from a
                   separate file.  You can do this in  either  "binary"  or
                   "journal" mode.  Journal files can be edited.  

                o  A  PASS_ON  command is included that allows you to force
                   UCL+ to "pass-on" a given command  string  to  the  next
                   program  in the chain (the default mode) or to a program
                   that you specify.  

                o  Symbol  expansions can be DISPLAYed with or without exe-
                   cution.  The DISPLAY command can also be used to  output
                   ASCII  strings  to  the  console  or  printer (handy for
                   sneaky escape sequences).  

                o  You  can enter and use virtually any character in a sym-
                   bol  definition,   including   eight-bit   and   control
                   characters.  

                o  You  may,  in  addition  to the symbol definitions, list
                   other program parameters as well.  List  output  may  be
                   directed to devices/files other than the console.  

                o  UCL+  can  be  employed,  via the UCI_MODE command, as a
                   "User Command Interface" (UCI).  This functionality  was
                   added with UCL+ V7 to take advantage of the UCI facility
                   in TSX-Plus.  

                o  You may dynamically redefine the prompt string issued by
                   UCL+.  

          UCL+ -- User Command Linkage Program - V08.02a             Page 7
                  Introduction


                o  A "quoting" facility is available to override the effect
                   of "operator" characters.  

                o  In order to allow more complex command definitions, UCL+
                   supports the parsing of argument strings into as many as
                   nine sub-strings.  

                o  You  may  define default values for argument strings and
                   argument sub-strings.  

                o  If you have an RT-11 V5.2 or later monitor, you can take
                   advantage of some additional features:  

                    -  A  CI  "handleroid"  is included which allows you to
                       control and display the action of the  various  Com-
                       mand Language Interpreters (CLIs).  For example, SET
                       CI UCF  turns  on  the  User  Commands  First  (UCF)
                       facility.  

                    -  A  special version of UCL+ is available for extended
                       memory monitors.  Almost the entire program is  con-
                       tinuously  resident  in  a global region in extended
                       memory.   It  is  very  fast,  and  uses  only   512
                       (decimal) words of low memory.  



          UCL+ -- User Command Linkage Program - V08.02a             Page 8
                  Installation


          6.0  INSTALLATION 

          This  section of the manual contains information on the installa-
          tion of the major components of  the  UCL+  distribution.   These
          are:  

                o  UCL.SAV - the "vanilla" UCL+ program (section 6.1) 

                o  UCLXM.SAV  -  a  special extended memory (XM) version of
                   UCL+ (section 6.2) 

                o  UCLXD.SAV  -  the  "external  data"  (XD) variant of the
                   "vanilla" UCL+ program (section 6.3) 

                o  CI.SYS  -  the Command Line Interpreter handler (section
                   6.4) 

                o  UCLHLP.TXT  -  the  help  text necessary to build a UCL+
                   help program (section 6.5) 

          The following is a list of who runs with what.  The program names
          in upper case denote the "recommended" version of UCL+  for  that
          particular  environment.   The  XM version is recommended when it
          offers performance advantages.  The  XD  version  is  flagged  in
          those  situations  where  maintenance  of "user-specific" context
          data may be an issue.  

                o  RT-11 V5.0, V5.1, all monitors:  UCL, uclxd 

                o  RT-11 V5.2 - V5.5, SJ and FB:  UCL, uclxd 

                o  RT-11 V5.2 - V5.5, XM:  ucl, uclxd, UCLXM 

                o  RT-11 V5.6 or later, SB and FB:  UCL, uclxd 

                o  RT-11 V5.6 or later, except SB, FB:  ucl, uclxd, UCLXM 

                o  TSX-Plus, V4.1:  UCL, uclxd 

                o  TSX-Plus, V5.x:  ucl, UCLXD 

                o  TSX-Plus, V6.0 or later:  ucl, UCLXD, uclxm 

                o  RTEM, any version with UCL support:  ucl, UCLXD 


          As  with  all sections of this document, a basic familiarity with
          RT-11 and, if applicable, TSX-Plus is assumed.  

          In  all of the examples in this section, the UCL+ distribution is
          assumed to be on  the  default  device,  DK:.   Examples,  unless
          otherwise  noted, will work on RT-11 V5.0 or later systems and/or

          UCL+ -- User Command Linkage Program - V08.02a             Page 9
                  Installation


          the  functionally  equivalent  version  of  TSX-Plus   or   RTEM.
          TSX-Plus  users should also note that the installation procedures
          for TSX assume that the user has sufficient privilege to  execute
          them  --  i.e.,  installation will be probably be accomplished by
          the system manager.  

          The  examples  also  assume that you are going to use the default
          program names when you install the various components.  There are
          cases  where  this may not be true (for example, if you alternate
          between two different RT-11 monitors on the same  machine).   See
          the application notes, sections 15.7 and 15.8, for information on
          changing these defaults.  

          If  you  are converting from any version of UCL+ prior to V07.50,
          you should also read section 8.5 and the application note in sec-
          tion 15.4.  

          Please remember that reasonable attempts are made to keep succes-
          sive  versions  of  UCL+  upward  compatible,  but  there  is  no
          guarantee  that  they  are downward compatible.  Thus, V7.55 will
          accept V7.54 journal files, but it is very unlikely  that  things
          will work the other way around.  


                            V07.54 OR EARLIER UCL+ USERS

               The  "CD"  and "RNO" commands are no longer included in
               the distributed UCL+ program.  "CD" can now be  defined
               as a symbol, as can a base-line "RNO" command.  See the
               application note,  section  15.11,  for  details.   The
               standard, hard-wired "RNO" command is also available as
               a conditional assembly (see section 15.6).  



          UCL+ -- User Command Linkage Program - V08.02a            Page 10
                  Installation


          6.1  Installing UCL.SAV 

          UCL.SAV  is  the  "vanilla" UCL+ program.  It will run under ver-
          sions of RT-11 beginning  with  V5.0  (and  the  equivalent  RTEM
          releases)  and  versions  of  TSX-Plus starting with V4.1.  As it
          does a context check on start-up, it is not necessary to generate
          a  special  version  for either operating system.  It is, in fact
          (and by design), possible to use the same copy of  UCL+  in  both
          environments.  The installation procedure may differ, however, in
          some cases.  


          6.1.1  Installing UCL.SAV On RT-11 Systems  - For all versions of
          RT-11, UCL+ serves as a direct replacement  for  the  distributed
          UCL  program  (note  that  the V5.0 distribution contained no UCL
          program).  For those versions of RT-11 supporting  User  Commands
          First (UCF), UCL+ can be used as a UCF also (except RTEM).  


                                       WARNING

               If you are using the Single-Line Editor (SL) and the SL
               "RECALL" command is enabled, issue the command  SET  SL
               NORECALL  prior  to  installing UCL+.  You can reenable
               the SL RECALL feature after  UCL+  is  installed.   See
               section 15.12 for more details.  




          6.1.1.1  Installation As A UCL (UCL.SAV => UCL.SAV)  - If you are
          already using a previous version of UCL+, you should  first  save
          your current symbol/status data.  For example, 

                    .STORE SY:CURENT                      _______________

          (Type  "STORE  SY:CURENT.UCL" if your old UCL+ is a V7.xx XM ver-
          sion.) 

          To install UCL.SAV, just copy it to the system device:  

                    .COPY UCL.SAV SY:UCL.SAV                      _______________________

          If you are not a previous UCL+ user, you're done.  Otherwise, the
          next step depends on whether your old UCL+ is V6x or not.  If  it
          is  V6x,  follow the procedure described in the application notes
          (section 15.3).  If it is V7.xx or later, you can just type 

                    .RECALL SY:CURENT                      ________________

          to load the symbol/status data into your new copy of UCL+.  


          UCL+ -- User Command Linkage Program - V08.02a            Page 11
                  Installation


          Note  that  the  above  procedure  is  the same for TSX-Plus V4.1
          users.  


          6.1.1.2  Installation  As A UCF (UCL.SAV => UCF.SAV)  - Beginning
          with V5.2, RT-11 supports User Commands First (UCF)  as  well  as
          UCL.  If you wish to use UCL+ as a UCF, you need only make a copy
          with the appropriate name and turn on UCF support in the monitor.
          Unless you are doing something sneaky, the installation procedure
          is as follows (note that  this  command  sequence  is  for  RT-11
          V5.2):  

                    .copy ucl.sav sy:ucf.sav                     _______________________

                    .r ucf                     _____
                    UCL> prompt "ucf> "                         ______________
                    ?UCL-I-Prompt changed to "ucf> "
                    ucf> <ctrl/C>                         ________

          The  easiest  way to invoke UCF processing is via the CI handler.
          I.e., 

                    .set ci ucf,show                     _______________
                    ?CI-I-CLIs enabled: UCF DCL CCL UCL

          When  UCL+  runs as UCF, it automatically detects this condition,
          and processes commands appropriately.  


          6.1.2  Installing  UCL.SAV On TSX-Plus Systems  - If you are run-
          ning TSX-Plus V4.1, installation is the same as it is  for  RT-11
          (section 6.1.1).  If you are running V5.0 or later, the procedure
          is somewhat different.  

          Note  that  you should make sure that UCL support is enabled when
          you execute your initial TSGEN.  

          Also  note that TSX-Plus users must have read/write access to the
          UCL+ program if they are to be able to define or  erase  symbols.
          The  easiest  way to accomplish this is to include an ACCESS com-
          mand in the user's logon command file.  For example:  

                    ACCESS SY:TSXUCL.SAV 


                                       WARNING

               If you are using the Single-Line Editor (SL) and the SL
               "RECALL" command is enabled, issue the command  SET  SL
               NORECALL  prior  to  installing UCL+.  You can reenable
               the SL RECALL feature after  UCL+  is  installed.   See
               section 15.12 for more details.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 12
                  Installation


          6.1.2.1  Installation  As A UCL (UCL.SAV => TSXUCL.SAV)  - If you
          are already using a previous version of UCL+,  you  should  first
          save your current symbol/status data.  For example, 

                    .STORE SY:CURENT                      _______________

          (Type  "STORE  SY:CURENT.UCL" if your old UCL+ is a V7.xx XM ver-
          sion.) 

          To install UCL.SAV, just copy it to the system device.  Note that
          the default TSX-Plus name for UCL is TSXUCL.SAV.  

                    .COPY UCL.SAV SY:TSXUCL.SAV                      __________________________

          If  you  are  not  a previous UCL+ user, you're done, and you can
          proceed to define the symbols that you intend to use.  Otherwise,
          the next step depends on whether your old UCL+ is V6x or not.  If
          it is V6x, follow the procedures  described  in  the  application
          notes (section 15.3).  If it is V7.xx or later, you can just type 

                    .RECALL SY:CURENT                      ________________

          to load the symbol/status data into your new copy of UCL+.  


          6.1.2.2  Installation As A UCI (UCL.SAV => UKMON.SAV)  - UCL+ can
          also be used on a TSX-Plus V5.0 or later system as a User Command
          Interface (UCI).  The following example illustrates a typical in-
          stallation with the default UCI name of UKMON.SAV.  Note that the
          command  prompt  is changed during this procedure to help distin-
          guish the "UCI" copy of UCL+ from other copies that  might  exist
          on the same system as "UCLs".  

                    .COPY UCL.SAV SY:UKMON.SAV                     _________________________
                    .R UKMON                     _______
                    UCL> uci "ukmon> "                         _____________
                    ?UCL-I-UCI_MODE enabled
                    ?UCL-I-Prompt changed to "ukmon> "
                    ukmon> <ctrl/C>                           ________

          You would invoke UKMON.SAV as a UCI by typing 

                    .SET KMON UCI                     ____________

          UCL+ -- User Command Linkage Program - V08.02a            Page 13
                  Installation


          6.2  Installing UCLXM.SAV 

          UCLXM.SAV  is  a  special  version  of UCL+ for use with extended
          memory (XM) monitors on systems running RT-11 V5.2 or later.   It
          can also be used under TSX-Plus monitors that are compatible with
          RT-11 V5.2 (TSX-Plus V6.0 or later).  

          UCLXM  has  a minimal low memory presence -- typically, about 512
          (decimal) words.  The remainder of the program, about 10K  words,
          resides in a global region in extended memory.  

          In  the RT-11 environment, UCLXM is significantly faster than the
          "vanilla" UCL+ due to the fact that all but a two-block "stub" is
          permanently  memory  resident.   UCLXM  is  a  direct, functional
          replacement  for  the  distributed  UCL  program.   As  with  the
          "vanilla" UCL+ program, UCLXM can also be used as a UCF program. 

          Under TSX-Plus, speed improvement resulting from the use of UCLXM
          instead of the regular UCL+ program will depend on  such  factors
          as  the  amount  of memory available for cache, and the amount of
          swapping normally seen on the system.  It is interesting to note,
          however,  that  the  "low memory" image of UCLXM is less than 512
          bytes (a user job size of 10kb under a V6.4  monitor).   This  is
          due  to the fact that the bulk of the program (20.5kb) resides in
          a shared global region.  If multiple copies of UCL+  are  running
          simultaneously,  they are all sharing the same global region and,
          thus, sharing most of their run-time code.  


                                     WARNING!!!

               Do not attempt to run UCLXM.SAV under a monitor that is
               not compatible with RT-11 V5.2 or later.   The  results
               are unpredictable -- your system may crash.  




          6.2.1  Installing UCLXM.SAV On RT-11 Systems  - Installing the XM
          version of UCL+ under RT-11 is a reasonably straightforward  pro-
          cess,  although  there  may be some special considerations if you
          are "porting" from a V6 version of UCL+.  

          All examples in this section are for an RT-11 V5.2 monitor.  


                                       WARNING

               If you are using the Single-Line Editor (SL) and the SL
               "RECALL" command is enabled, issue the command  SET  SL
               NORECALL  prior  to  installing UCL+.  You can reenable

          UCL+ -- User Command Linkage Program - V08.02a            Page 14
                  Installation


               the SL RECALL feature after  UCL+  is  installed.   See
               section 15.12 for more details.  




          6.2.1.1  Installation  As  A UCL (UCLXM.SAV => UCL.SAV)  - If you
          are already using a previous version of UCL+,  you  should  first
          save your current symbol/status data.  For example, 

                    .store sy:curent                      _______________

          (Type  "store  sy:curent.ucl" if your old UCL+ is a V7.xx XM ver-
          sion.) 

          If  your  previous  version  of UCL+ was also the XM version, you
          should REMOVE the global region.  

                    .remove ucl                      __________

          To install UCLXM.SAV, copy it to the system device as UCL.SAV.  

                    .copy uclxm.sav sy:ucl.sav                      _________________________

          If  you  are  not  a previous UCL+ user, you're done, and you can
          proceed to define the symbols that you intend to use.  Otherwise,
          the  next step depends on whether your old UCL+ was V6x or V7.xx.
          If it was V6x, see the application note in section 15.3.   If  it
          is V7.xx or later, just type 

                    .recall sy:curent                      ________________

          to  load  the  symbol/status  data  into  your  new copy of UCL+.
          (Note:  If the extension of the file you  are  RECALLing  is  not
          .UCL, you will need to enter the extension explicitly.) 

          Finally,  it  is  a  good  idea to run UCL and change the command
          prompt.  

                    .r ucl                     _____
                    UCL> prompt "uclxm> "                         ________________
                    ?UCL-I-Prompt changed to "uclxm> "
                    uclxm> <ctrl/C>                           ________


          6.2.1.2  Installation   As   A   UCF   (UCLXM.SAV   =>   UCF.SAV)
          Beginning with V5.2, RT-11 supports User Commands First (UCF)  as
          well  as UCL.  If you wish to use UCL+ as a UCF, you need to make
          a copy with the appropriate name and turn on UCF support  in  the
          monitor.   Unless  you  plan to do something sneaky (like letting
          UCL and UCF share the same global region  --  risky!),  you  must
          also  patch  your  UCF  so that it will establish its own, unique

          UCL+ -- User Command Linkage Program - V08.02a            Page 15
                  Installation


          global region in extended memory.  The installation procedure  is
          as follows.  

          Remove  the UCF global region and create a new copy of UCF.SAV on
          SY:.  

                    .remove ucf                     __________

                    .copy uclxm.sav sy:ucf.sav                     _________________________

          Next,  apply  the  customization  patch to cause UCF.SAV to use a
          unique global region.  

                    .sipp sy:ucf.sav/a                     _________________
                    Base?    <ret>                             _____
                    Offset?  1024                             ____

                      Base       Offset      Old  New?
                       000000     001024  101704  ;R                                                  __
                       000000     001024   <UCL>  ;RUCF                                                  _____
                       000000     001026   <   >  <ctrl/Y>                                                  ________

          Following this, it is recommended that you run UCF and change the
          command prompt.  

                    .r ucf                      _____
                    UCL> prompt "ucfxm> "                          ________________
                    ?UCL-I-Prompt changed to "ucfxm> " 
                    ucfxm> <ctrl/C>                            ________

          The  easiest  way to invoke UCF processing is via the CI handler.
          I.e., 

                    .set ci ucf,show                     _______________
                    ?CI-I-CLIs enabled: UCF DCL CCL UCL

          When  UCL+  runs as UCF, it automatically detects this condition,
          and processes commands appropriately.  


          6.2.2  Installing UCLXM.SAV On TSX-Plus Systems  - Installing the
          XM version of UCL+ under TSX-Plus is similar to  the  RT-11  pro-
          cedure.   As with RT-11, there may be some special considerations
          if you are "porting" from an earlier, non-XM version of UCL+.  

          In  addition, the XM version of UCL+ must be able to use TSX-Plus
          global region support.   This  can  be  accomplished  by  editing
          TSGEN.MAC  prior  to building TSX-Plus, or through the use of the
          INSTALL command.  PRO/TSX-Plus users must use  the  INSTALL  com-
          mand,  since  TSGEN.MAC  is not included in the PRO distribution.
          For a V6.4 monitor, the command is as follows 


          UCL+ -- User Command Linkage Program - V08.02a            Page 16
                  Installation


                    install add sy:tsxucl.sav/priv=(nodebug,sysgbl) 

          The  best  place to put this command is in a detached job command
          file that is executed when TSX-Plus is booted.  

          Also  note that TSX-Plus users must have read/write access to the
          UCL+ program if they are to be able to define or  erase  symbols.
          The  easiest  way to accomplish this is to include an ACCESS com-
          mand in the user's logon command file.  For example:  

                    ACCESS SY:TSXUCL.SAV 

          All examples in this section are for a TSX-Plus V6.0 monitor.  


                                       WARNING

               If you are using the Single-Line Editor (SL) and the SL
               "RECALL" command is enabled, issue the command  SET  SL
               NORECALL  prior  to  installing UCL+.  You can reenable
               the SL RECALL feature after  UCL+  is  installed.   See
               section 15.12 for more details.  




          6.2.2.1  Installation  As  A  UCL (UCLXM.SAV => TSXUCL.SAV)  - If
          you are already using a previous  version  of  UCL+,  you  should
          first save your current symbol/status data.  For example, 

                    .store sy:curent                      _______________

          (Type  "store  sy:curent.ucl" if your old UCL+ is a V7.xx XM ver-
          sion.) 

          If  your  previous  version  of UCL+ was also the XM version, you
          should REMOVE the global region.  E.g., 

                    .remove ucl                      __________

          To install UCLXM.SAV, copy it to the system device as TSXUCL.SAV. 

                    .copy uclxm.sav sy:tsxucl.sav                      ____________________________

          If  you  are  not  a previous UCL+ user, you're done, and you can
          proceed to define the symbols that you intend to use.  Otherwise,
          the  next step depends on whether your old UCL+ was V6x or V7.xx.
          If it was V6x, see the application note in section 15.3.   If  it
          is V7.xx or later, just type 

                    .recall sy:curent                      ________________


          UCL+ -- User Command Linkage Program - V08.02a            Page 17
                  Installation


          to load the symbol/status data into your new copy of UCL+.  

          Finally,  it  is a good idea to run TSXUCL and change the command
          prompt.  

                    .r tsxucl                     ________
                    UCL> prompt "tsxucl> "                         _________________
                    ?UCL-I-Prompt changed to "tsxucl> "
                    tsxucl> <ctrl/C>                            ________


          6.2.2.2  Installation  As A UCI (UCLXM.SAV => UKMON.SAV)  - Under
          TSX-Plus, UCL+ can also be  used  as  a  User  Command  Interface
          (UCI).   The following example illustrates a typical installation
          with the default UCI name of UKMON.SAV.  Note that  the  name  of
          the  global  region used by UKMON.SAV is changed from the default
          value of "UCL".  Note also that the  command  prompt  is  changed
          during  this procedure to help distinguish the "UCI" copy of UCL+
          from other copies that might exist on the same system as "UCLs". 

                    .copy uclxm.sav sy:ukmon.sav                     ___________________________
                    .sipp sy:ukmon.sav/a                     ___________________
                    Base?    <ret>                             _____
                    Offset?  1024                             ____

                      Base       Offset      Old  New?
                       000000     001024  101704  ;R                                                  __
                       000000     001024   <UCL>  ;RUKM                                                  _____
                       000000     001026   <   >  ;RON                                                  ____
                       000000     001030   < FP>  <ctrl/Y>                                                  ________
                    .r ukmon                     _______
                    UCL> uci "ukmon> "                         _____________
                    ?UCL-I-UCI_MODE enabled
                    ?UCL-I-Prompt changed to "ukmon> "
                    ukmon> <ctrl/C>                           ________

          You would invoke UKMON.SAV as a UCI by typing 

                    .set kmon uci                     ____________

          UCL+ -- User Command Linkage Program - V08.02a            Page 18
                  Installation


          6.3  Installing UCLXD.SAV 

          UCLXD.SAV  is  the  "external data" (XD) variant of the "vanilla"
          UCL+ program, UCL.SAV.  The two programs differ in the  way  that
          they  maintain  their  context areas.  When you do something that
          changes the UCL+ context (define a symbol, issue a PATH  command,
          etc.),  UCL.SAV  "memorizes" this action by posting the change to
          its own disk image.  Thus, UCL.SAV updates its context area  "in-
          ternally."  In  contrast,  UCLXD.SAV  keeps its context area in a
          separate disk file named UCLPLS.DAT;  it updates context  "exter-
          nally." 

          UCLXD.SAV  will  run  under versions of RT-11 beginning with V5.0
          (and the equivalent  RTEM  releases)  and  versions  of  TSX-Plus
          starting  with  V4.1.  Since it does a context check on start-up,
          it is not necessary to generate  a  special  version  for  either
          operating  system.   It  is, in fact (and by design), possible to
          use the same copy of UCL+ in both environments.  However, the in-
          stallation procedure may differ in some cases.  

          UCLXD.SAV  is  the  recommended UCL+ program for TSX-Plus V5.x or
          later, and RTEM.  


          6.3.1  Installing  UCLXD.SAV On RT-11 Systems  - For all versions
          of RT-11, UCL+ serves as a direct replacement for the distributed
          UCL  program  (note  that  the V5.0 distribution contained no UCL
          program).  For those versions of RT-11 supporting  User  Commands
          First (UCF), UCL+ can be used as a UCF also (except RTEM).  


                                       WARNING

               If you are using the Single-Line Editor (SL) and the SL
               "RECALL" command is enabled, issue the command  SET  SL
               NORECALL  prior  to  installing UCL+.  You can reenable
               the SL RECALL feature after  UCL+  is  installed.   See
               section 15.12 for more details.  




          6.3.1.1  Installation  As  A UCL (UCLXD.SAV => UCL.SAV)  - If you
          are already using a previous version of UCL+,  you  should  first
          save your current symbol/status data.  For example, 

                    .STORE SY:CURENT                      _______________

          (Type  "STORE  SY:CURENT.UCL" if your old UCL+ is a V7.xx XM ver-
          sion.) 

          To install UCLXD.SAV, just copy it to the system device:  

          UCL+ -- User Command Linkage Program - V08.02a            Page 19
                  Installation



                    .COPY UCLXD.SAV SY:UCL.SAV                      _________________________

          Next, you should set up the UCL+ data device.  I.e., 

                    .ASSIGN xd-device UCL:                       _____________________

          where  "xd-device"  is  the  device where UCL+ external data file
          will be kept.  It's a good idea to place  this  command  in  your
          start up command file.  

          UCLXD.SAV  maintains  its  symbol/status data in an external data
          file named UCLPLS.DAT.  UCLXD.SAV looks for this file  on  device
          "UCL:." If the file is not found, it looks on SY:.  

          If  UCLPLS.DAT  already  exists,  you're  done.   If not, you can
          create it at this point by running the UCL+ program:  

                    .R UCL                      _____
                    ?UCL-I-Data file not found;  creating new one 
                    UCL> <ctrl/C>                          ________

          If  you have assigned UCL:, the data file will be created on that
          device.  Otherwise, it will be created on the system device, SY:. 

          If  you are converting to the XD variant of UCL+ from a previous,
          non-XD, version, you will need to  load  the  symbol/status  data
          into  your new copy of UCL+.  If your old UCL+ is V6x, follow the
          procedures described in section 15.3.  If it is V7.xx  or  later,
          simply type 

                    .RECALL SY:CURENT                      ________________

          to load the symbol/status data into your new copy of UCL+.  

          Note  that  the  above  procedure  is  the same for TSX-Plus V4.1
          users.  


          6.3.1.2  Installation   As   A   UCF   (UCLXD.SAV   =>   UCF.SAV)
          Beginning with V5.2, RT-11 supports User Commands First (UCF)  as
          well  as UCL.  If you wish to use UCLXD.SAV as a UCF, the follow-
          ing is a  reasonable  installation  procedure.   (Note:   If  you
          desire  to  preserve  the symbol/status data from an existing UCF
          program, use the techniques described in  the  previous  section,
          6.3.1.1.   Also  note  that  the  command sequences are for RT-11
          V5.2.) 

          Copy UCLXD.SAV to the system device as file UCF.SAV.  

                    .copy uclxd.sav sy:ucf.sav                     _________________________


          UCL+ -- User Command Linkage Program - V08.02a            Page 20
                  Installation


          At  this point, it is strongly recommended that you patch UCF.SAV                                ________
          to change the name of the external data file used  by  this  pro-
          gram.   "UCFPLS.DAT"  is  a  good  choice.   You may also wish to
          change the default external data device mnemonic  from  "UCL"  to
          "UCF."  The procedure for making these modifications is described
          in the application notes, section 15.16.  

          Once UCF.SAV has been patched, assign its data device.  E.g., 

                    assign xd-device ucf:  

          where "xd-device" is the name of the device that will contain the
          UCF external data file.  

          If  the  external data file already exists, you're done.  If not,
          you can create it at this point by running the program  directly.
          While you're at it, it's also a good idea to change the program's
          prompt.  

                    .r ucf                      _____
                    ?UCL-I-Data file not found;  creating new one 
                    UCL> prompt "ucf> "                          ______________
                    ?UCL-I-Prompt changed to "ucf> " 
                    ucf> <ctrl/C>                          ________

          The  easiest  way to invoke UCF processing is via the CI handler.
          I.e., 

                    .set ci ucf,show                     _______________
                    ?CI-I-CLIs enabled: UCF DCL CCL UCL

          When  UCL+  runs as UCF, it automatically detects this condition,
          and processes commands appropriately.  


          6.3.2  Installing  UCLXD.SAV  On  TSX-Plus  Systems  - If you are
          running TSX-Plus V4.1, installation is the  same  as  it  is  for
          RT-11  (section  6.3.1).   If  you are running V5.0 or later, the
          procedure is somewhat different.  

          You should make sure that UCL support is enabled when you execute
          your initial TSGEN.  

          Also,  TSX-Plus users must have read/write access to the UCL+ ex-
          ternal data (XD) file if they are to be able to define  or  erase
          symbols.   The  easiest  way to accomplish this is to include the
          appropriate commands in the user's logon command file.   The  de-
          tails will depend on your system layout.  

          If  each  user  is  assigned  a  private  work area at logon time
          (usually a logical device), this can be designated as the UCL+ XD
          device also.  For example, 

          UCL+ -- User Command Linkage Program - V08.02a            Page 21
                  Installation



                    MOUNT LD0 DU1:FRED.DSK DK 
                    ASSIGN DK UCL 

          This technique results in each user having their own private copy
          of the XD file UCLPLS.DAT and, thus, their  own  "local"  set  of
          symbol definitions.  

          If  you  want  all of your users to have read/write access to one
          central copy of UCLPLS.DAT, the command sequence might  be  some-
          thing like this:  

                    ACCESS SY:UCLPLS.DAT 

          This  approach gives "global" access to the UCL+ facilities;  all
          users on the system have a common set of symbol definitions.  


                                       WARNING

               If you are using the Single-Line Editor (SL) and the SL
               "RECALL" command is enabled, issue the command  SET  SL
               NORECALL  prior  to  installing UCL+.  You can reenable
               the SL RECALL feature after  UCL+  is  installed.   See
               section 15.12 for more details.  




          6.3.2.1  Installation As A UCL (UCLXD.SAV => TSXUCL.SAV)  - Under
          TSX-Plus, you may install the external data (XD) version of  UCL+
          either  "locally"  or  "globally." Local installation causes each
          user to have their own set of symbol definitions;  global instal-
          lation results in all users having access to a common set of sym-
          bols.  (It is also possible to have both local and global sets --
          see application note 15.17.) As discussed in the previous section
          (6.3.2), the XD version's behavior, once  installed,  depends  on
          the  assignment  of  the  logical mnemonic "UCL." Aside from this
          consideration, the installation procedure is as follows:  

          If  you  are already using a previous version of UCL+, you should
          first save your current symbol/status data.  For example, 

                    .store sy:curent                      _______________

          (Type  "store  sy:curent.ucl" if your old UCL+ is a V7.xx XM ver-
          sion.) 

          Next, copy UCLXD.SAV to the system device.  Note that the default
          TSX-Plus name for UCL is TSXUCL.SAV.  

                    .copy uclxd.sav sy:tsxucl.sav                      ____________________________

          UCL+ -- User Command Linkage Program - V08.02a            Page 22
                  Installation



          The XD version of UCL+ maintains its symbol/status data in an ex-
          ternal data file named UCLPLS.DAT.  It looks  for  this  file  on
          device  "UCL:."  If  the file is not found, it looks on SY:.  For
          global installation under TSX-Plus, the mnemonic  "UCL:"  is  not
          normally defined.  

          If  UCLPLS.DAT  already  exists,  you're done.  If not, this file
          will automatically be created the first time UCL+ is run.  (A de-
          tailed  discussion  of XD file initialization can be found in the
          application notes, section 15.14.) In the following  example,  an
          XD  file  is created by running UCL+ directly.  The prompt string
          is changed also.  

                    .r tsxucl                      ________
                    ?UCL-I-Data file not found;  creating new one 
                    UCL> prompt "tsxucl> "                          _________________
                    ?UCL-I-Prompt changed to "tsxucl> " 
                    tsxucl> <ctrl/C>                             ________

          If  you have assigned UCL:, the data file will be created on that
          device.  Otherwise, it will be created on the system device, SY:. 

          If  you are converting to the XD variant of UCL+ from a previous,
          non-XD version, you will need to load the symbol/status data into
          your  new copy of UCL+.  If your old UCL+ is V6x, follow the pro-
          cedures described in section 15.3.  If it is V7.xx or later, sim-
          ply type 

                    .r tsxucl                      ________
                    tsxucl> recall sy:curent                             ________________
                    tsxucl> <ctrl/C>                             ________


          6.3.2.2  Installation  As  A UCI (UCLXD.SAV => UKMON.SAV)  - UCL+
          can be used on a TSX-Plus V5.0 or later system as a User  Command
          Interface  (UCI).  It should be pointed out, however, that the XD
          version of UCL+ requires the most  complicated  UCI  installation
          procedure.   The  non-XD  version  (section 6.1.2.2) is usually a
          better choice for the majority of applications.  The  XM  version
          can also be used (section 6.2.2.2).  

          The  following  example illustrates a typical UCI installation of
          UCLXD.SAV with the default name of UKMON.SAV.  

          Note  that  the  name  of  the  external  data file is changed to
          UKMON.DAT in order to avoid potential conflicts with  the  system
          UCL  program.  (At the time this document was prepared, the value
          that you should substitute for "XDFIL"  was  036402  --  you  can
          verify this by checking the UCL+ link map, UCL.MAP.) 


          UCL+ -- User Command Linkage Program - V08.02a            Page 23
                  Installation


          The  device  mnemonic  for the XD file could also be changed from
          "UCL" to "SY." This would force the UCI  program  to  obtain  its
          symbol  status  data  from  a  single, central file on the system
          device.  (A more complete discussion of the procedure for  chang-
          ing the XD file name and device can be found in section 15.16.) 

          Note  also  that  when UCI_MODE is enabled, the command prompt is
          changed as well.  This helps to distinguish  the  "UCI"  copy  of
          UCL+  from  other  copies  that might exist on the same system as
          "UCLs." 

                    .copy uclxd.sav sy:ukmon.sav                     ___________________________
                    .sipp ukmon.sav/a                     ________________
                    Base?    <ret>                             _____
                    Offset?  XDFIL                             _____

                      Base       Offset      Old  New?
                       000000     XDFIL   101704  ;R                                                  __
                       000000     XDFIL    <UCL>  ;RUKM                                                  _____
                       000000     XDFIL+2  <PLS>  ;RON                                                  ____
                       000000     XDFIL+4  <DAT>  <ctrl/Y>                                                  ________

                    .r ukmon                     _______
                    UCL> uci "ukmon> "                         _____________
                    ?UCL-I-UCI_MODE enabled
                    ?UCL-I-Prompt changed to "ukmon> "
                    ukmon> <ctrl/C>                           ________

          You would invoke UKMON.SAV as a UCI by typing 

                    .set kmon uci                      ____________

          UCL+ -- User Command Linkage Program - V08.02a            Page 24
                  Installation


          6.4  Installing The CI Handler 

          The CI (Command line Interpreter) handler can be  used  on  RT-11
          V5.2  or  later systems to control the action of the various com-
          mand line interpreters (CLIs).  It contains no executable handler                                                      _____________________
          code;   all  it  does  is execute SET commands.  Installation is,          ____
          therefore, very simple.  Just copy CI.SYS to your system  device,
          giving it the name appropriate to your particular monitor.  

          For non-extended memory versions of the RT-11 monitor:  

                    .copy/sys ci.sys sy:                     ___________________

          For extended memory monitors:  

                    .copy/sys ci.sys sy:cix.sys                     __________________________

          See section 10.0 for more information in the CI handler.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 25
                  Installation


          6.5  Installing UCL+ HELP 

          The UCL+ distribution includes a help-text file named UCLHLP.TXT.
          You can use this file to set up on-line help text for  UCL+  com-
          mands in one of two ways:  

                o  The  most  general,  and most tedious, method is to edit
                   the HELP macros contained in  UCLHLP.TXT  into  HELP.TXT
                   and  then  rebuild  the HELP program.  This technique is
                   described in the RT-11 Installation Guide.  If  you  are
                   using  version  5.1  or later of RT-11, you will have to
                   use SPLIT.SAV to create HELP.EXE and HELP.TXT (see  file
                   UNSUP.TXT  on  the  RT-11  distribution kit).  Note that
                   both the RT-11 and UCL+ help text files contain a  macro
                   named  "HELP."  You  should  retain the RT-11 version of
                   this macro.  

                o  The  second approach involves the creation of a separate
                   HELP program for UCL+.  In this case, you create a macro
                   library from UCLHLP.TXT, build a secondary HELP program,
                   and define a symbol (I like to use HLP)  to  invoke  it.
                   The  following  example  assumes  that  you are using RT
                   V5.1.  All required files  are  assumed  to  be  on  the
                   default device (DK:).  

                      .SPLIT HELP.EXE=HELP.SAV/B:10                        ____________________________

                      .LIB/MAC UCLHLP UCLHLP.TXT                        _________________________

                      .COP HELP.EXE+UCLHLP.MLB UCLHLP.SAV                        __________________________________

                      .COP UCLHLP.SAV SY:                         __________________

                      .HLP==R UCLHLP\^                        _______________



                                        NOTE

               If  you are using a version of RT-11 prior to V5.2, the
               SPLIT boundaries are different for  HELP.SAV.   In  the
               above  example,  the  value  for the "/B" switch in the
               first line becomes 7 instead of 10.  This boundary may,
               of course, change again in later versions of RT-11.  



          UCL+ -- User Command Linkage Program - V08.02a            Page 26
                  Installation


          6.6  Installing The UCL+ Distribution Under RTEM 

          The  following  special  considerations and restrictions apply to
          using the UCL+ package under the RT-11 Emulator (RTEM):  

                o  Use  the external data (XD) version of UCL+ (UCLXD.SAV).
                   The system manager should place UCLXD  in  the  "shared"
                   portion  of  the  virtual system device as file UCL.SAV.
                   If, for some reason, the non-XD version of UCL+ is  used
                   (UCL.SAV), a copy of this program must be placed in each
                   user's "private" area, and the distributed  UCL  program
                   deleted  from the shared area.  Otherwise, the installa-
                   tion procedure is essentially the same as for RT-11 sys-
                   tems (section 6.1.1.1).  

                o  If  it is to be used, the CI handler should be placed in
                   the "mark zone" portion of the  virtual  system  device.
                   This  is  normally  done by the system manager.  Section
                   6.4 contains  further  information  on  installing  this
                   handler.  

                o  The  UCL+  help  facility  is  normally installed in the
                   shared area of the virtual system device.   See  section
                   6.5  for further information on installing the UCL+ help
                   text.  

                o  Later versions of RTEM use the UCF facility to implement
                   specialized commands for this  environment.   Thus,  the
                   UCF facility is not available to RTEM users.  


          UCL+ -- User Command Linkage Program - V08.02a            Page 27
                  How It Works


          7.0  HOW IT WORKS 

          First,  read  the appropriate sections of the RT-11 Software Sup-
          port Manual (for  version  5.0,  this  is  sections  2.2.4.1  and
          2.2.4.2  --  pages  2-39 through 2-41).  If you are running RT-11
          version 5.2 or later, and you are  interested  in  User  Commands
          First  (UCF),  read  that stuff too.  TSX-Plus users should check
          out the additional material in the TSX manuals  on  User  Command
          Interfaces (UCIs) and the UCL SET commands.  

          OK,  now  that  you've  done your homework (and saved me a lot of
          typing)...  


          7.1  RT-11 Command Processing With UCL Support 

          As  you  will recall, if you are using a version of RT-11 that is
          sysgened to support User Command Linkage, RT goes through a  cer-
          tain  logical  sequence  to  evaluate  a command line.  First, it
          looks at the first word to see if this a valid RT-11 command.  If
          not,  it  looks  on  the system device (SY:) for a program to run
          that has the  same  name  as  this  first  word  (let's  call  it
          "word1").  If "SY:word1.SAV" is not found, it runs SY:UCL.SAV (if
          it exists) and passes the entire command line to UCL.  

          UCL+  understands  two  types of commands:  "hard-wired" commands
          (LIST or RECALL, for example),  which  are  "built  in"  to  UCL+
          (hereafter  referred  to  simply  as  "commands"), and "symbols",
          which are commands that you define (or modify or delete) from the
          console.  

          When  UCL+  receives  a  command  line, it first checks to see if
          word1 is a valid  command  and,  if  so,  calls  the  appropriate
          routine.   If  the  command  check  fails, UCL+ looks for a match
          against the currently defined symbols and, if successful, invokes
          the symbol processing stuff.  

          Next,   if   the  PATH  command  is  turned  on,  UCL+  uses  the
          "run-by-name" path to look for a  program  named  "dev:word1.SAV"
          (the  default  is dev=DK) and, if it finds it, runs it by passing
          the command "RUN command-string" to RT-11.  

          Finally,  if  all  else  fails, UCL+ exits with a "?UCL-E-Invalid
          command" error message or, if the CHAIN  command  is  in  effect,
          UCL+  chains to the specified program, and passes it the original
          command line.  


          UCL+ -- User Command Linkage Program - V08.02a            Page 28
                  How It Works


          In summary then, when you enter a command:  

               1)  RT-11 tries to execute it, then
               2)  RT-11 tries to run it off SY:, then
               3)  UCL+ tries to execute it as a command, then
               4)  UCL+ tries to execute it as a symbol, then
               5)  UCL+ tries to "run-by-name", then
               6)  you either get a nasty comment or UCL+ chains to another
                   program.



          7.2  RT-11 Command Processing With UCF Support 

          If your RT-11 is version 5.2 or later, you have support available
          for User Commands First (UCF) processing.  If you turn  UCF  sup-
          port  on  (this  can  be  done  with the CI handler;  see section
          10.0), RT-11 will collect your command line and,  after  checking
          for  IND  syntax, pass it directly to a program named SY:UCF.SAV.
          You can use UCL+ as a "UCF" by making a copy of it named UCF.SAV.
          UCL+  will  now  be intercepting commands before the monitor gets                                                    ______
          them!  This can get really tricky because  UCF  can,  in  effect,
          override normal RT-11 commands.  The implications of all this can
          get pretty complicated and are beyond the scope of  this  manual;
          read the RT-11 documentation and release notes for details.  

          The  main  thing  to remember is that UCL+ processes unrecognized
          commands differently when it is running as UCF than it does  when
          it  is running as UCL.  As UCF, it passes unknown commands to the
          monitor;  as UCL it issues an error message.  This  makes  sense,
          because UCF gets commands first while UCL gets them last.  

          The simplest situation, with UCF support turned on and UCL turned
          off, causes command  lines  to  be  processed  in  the  following
          sequence:  

               1)  UCF tries to execute it as a command, then
               2)  UCF tries to execute it as a symbol, then
               3)  UCF tries to "run-by-name", then
               4)  RT-11 tries to execute it, then
               5)  RT-11 tries to run it off SY:, then
               6)  you get "?KMON-F-Invalid command"



          7.3  TSX-Plus Command Processing 

          If you are using UCL+ with TSX-Plus version 4.1, things work more
          or less the same  as  they  do  with  RT-11  (see  section  7.1):
          TSX-Plus  passes the command string to UCL+ only if KMON fails to
          recognize it.  Things get a little more complicated, however,  if
          you are running under a V5.0 or later monitor.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 29
                  How It Works


                o  TSX-Plus  V5.0  looks  for  a "UCL" named SY:TSXUCL.SAV.
                   Version 4.1 uses the same name as RT-11 (SY:UCL.SAV).  

                o  Version  5  implements  a  UCL SET option.  SET UCL NONE
                   turns off user command linkage.  (Now who would want  to
                   do that?) SET UCL LAST causes command processing to work
                   like   it   did   under   V4.1   (except   you   get   a
                   "?KMON-F-Unrecognizable  command"  error message instead
                   of "?UCL-E-Invalid command").   SET  UCL  MIDDLE  allows
                   TSXUCL  to  examine  the  command string after it is in-
                   spected for a match against the  monitor  commands,  but
                   before  command  file/run-by-name  processing.   SET UCL
                   FIRST causes TSXUCL to be invoked prior to all KMON pro-
                   cessing  (i.e.,  it works like the RT-11 UCF facility --
                   see section 7.2).  Note that MIDDLE  will  cause  UCL+'s
                   run-by-name  path  to  take  priority over TSX's;  FIRST
                   will, in addition, give priority to UCL+  commands  over
                   KMON  commands  (i.e.,  you can replace monitor commands
                   with UCL+ commands).  

                o  Unless  UCL  is  set  FIRST, the monitor DISPLAY command
                   will preempt the UCL+ DISPLAY command.  This means  that
                   you  will need to define a symbol in order to invoke the
                   UCL+ DISPLAY command properly (for example, DSPLAY==_d). 

                o  UCL+  can also be used, under TSX, as a User Command In-
                   terface (UCI).  When UCI support is turned on  (via  the
                   SET  KMON UCI command), the UCI effectively replaces the                                                               ________
                   keyboard monitor (note that this is different  from  SET
                   UCL  FIRST  where  KMON  collects  the command, and then
                   passes it to UCL).  UCL+ can be used as a UCI by  making
                   a  copy  of it with the appropriate name (the default is
                   SY:UKMON.SAV) and utilizing the UCL+ UCI_MODE command.  


          See the TSX-Plus user documentation for further information.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 30
                  Symbols


          8.0  SYMBOLS 

          This is probably the most important section of this manual.  

          The  main  reason  for  using UCL+ (unless you just don't like to
          have a lot of empty space on your disk) is that it gives you  the
          ability  dynamically  to  define your own commands.  For the pur-
          poses of this  document,  these  user-defined  commands  will  be
          referred  to as "symbols".  The following sections present a sum-
          mary of how to define and manipulate these symbols.  


          8.1  Defining Symbols 

          Symbols  are  defined by entering a "symbol definition string" in
          the format 

                              symbol==definition 

          where  "symbol"  is  the  command  you are defining (6 characters
          max.), "==" is the symbol definition operator,  and  "definition"
          is the character-string (72 characters max.) that will govern the
          way that the symbol is replaced  (expanded)  when  it  is  inter-
          preted.  


                                        NOTE

               DEC's UCL uses a more "VMS-like" structure for defining
               symbols (possible  example:   REB*OOT:==BOOT DL0:   vs.
               REBOOT==BOOT DL0:).  UCL+ will accept the DEC format as
               well as the "normal" one.  However, the colon (":")  in
               the symbol definition operator and, if present, the em-
               bedded asterisk ("*"), will be ignored.  Note also that
               an  embedded  asterisk  remains undisturbed if the UCL+
               symbol definition operator ("==") is used.  


          In the simplest case, suppose you define the  symbol  "BUILD"  by
          entering 

                              BUILD==EX/MAC/NORUN

          If you subsequently enter

                              BUILD MYFILE

          this line is interpreted by UCL+ and passed back to RT-11 as

                              EX/MAC/NORUN MYFILE


          UCL+ -- User Command Linkage Program - V08.02a            Page 31
                  Symbols


          You  may  also  get  multiple-line  definitions via the backslash
          ("\") character.  For example, the symbol "WHEN" defined as 

                              WHEN==DATE\TIME 

          executes as if you had typed 

                              DATE 
                              TIME 

          A "^" character or characters in the definition governs where the
          "argument-part" of the input command string is  inserted  when  a
          symbol is expanded.  Thus, 

                              BUILD==EX/MAC/NORUN 

          and 

                              BUILD==EX/MAC/NORUN ^ 

          are  equivalent  symbol  definitions.  The "^" operator is really
          handy when the "argument-part" is to be embedded in the middle of
          the  expansion  somewhere  rather  than  tacked  on the end.  For
          example:  

                              VERSIO==RESORC SY:^.SAV/V 

          If you type 

                              VERSION PIP 

          this symbol will expand as 

                              RESORC SY:PIP.SAV/V 

          Finally, you may precede the "definition-part" with an underscore
          character ("_").  This will cause UCL+ to process the symbol  ex-
          pansion  in  "execute-immediate"  mode.   In other words, you are
          telling UCL+ that you are defining one symbol in terms of another
          symbol  or hard-wired command.  Thus, the expanded symbol is pro-
          cessed immediately by UCL+ rather than being passed on  to  RT-11
          as  a  command string.  This speeds up command execution substan-
          tially.  

          For example, 

                              SAY==DISPLAY "^"   (example 1) 

          and 

                              SAY==_DISPLAY "^"  (example 2) 


          UCL+ -- User Command Linkage Program - V08.02a            Page 32
                  Symbols


          are functionally equivalent definitions.  If you type 

                              SAY HELLO 

          both will expand (on the first pass through UCL+) as 

                              DISPLAY "HELLO" 

          But,  in  the  first  instance,  the UCL+ program will be invoked          ___
          twice:  once to expand SAY HELLO and  pass  the  string  back  to
          RT-11,  and  a  second  time  to execute DISPLAY "HELLO".  In the
          second example, UCL+ expands the command and then immediately ex-
          ecutes  the  resultant  command string.  Thus, example 2 executes
          much faster, especially on a floppy-based system, because UCL+ is
          only run once to process it, instead of twice.  

          Note  that  you are restricted to using "_" with definitions that
          expand to a single line.  

                              A==_B\C\D 

          will not work correctly (well, not in this version anyways).  


          8.2  Deleting Symbols 

          Individual  symbols can be deleted either by redefining them with
          a null definition or with the ERASE command.  For  example,  sup-
          pose you have defined a symbol TEMP as 

                              TEMP==EDIT MYFILE.MAC\DELETE MYFILE.BAK 

          You can delete this symbol by typing 

                              TEMP== 

          (UCL+  will  display  the message "?UCL-I-Erased symbol TEMP") or
          you can type 

                              ERASE TEMP 

          with  the  same effect.  If you wish to delete more than one sym-
          bol, the ERASE command is more efficient  (see  section  9.3  for
          more details on the ERASE command).  


          8.3  Entering Special Characters 

          There  are  a number of characters that cannot be typed directly.
          Examples of these "special" characters include control characters
          intercepted  by RT-11 (control-O, control-S, etc.), and eight-bit
          codes recognized by some of the newer terminals and printers.  If

          UCL+ -- User Command Linkage Program - V08.02a            Page 33
                  Symbols


          you  need to include a character of this type in a symbol defini-
          tion, you can do so by entering its value in the form 

                              <nnn>        for octal numbers, or 

                              <nnn.>       for decimal values, 

          where "nnn" is a number of up to three digits.  

          For example, to define a symbol, "BELL", which will ring the bell
          on the console:  

                              BELL==_D "<007> 

          Actually, it is not necessary to enter all three digits;  you may
          omit the leading zeros.  Thus, the bell character could  also  be
          represented as "<07>" or "<7>".  

          Note  that  UCL+ treats an invalid "<nnn>" sequence as if it were
          just a normal string of characters.  Thus, "<507>" would  not  be
          translated  into  a  character  because  507  is  too big to be a
          one-byte value (the maximum value is 377 octal or 255.  decimal).
          Likewise,  "<209>" would be ignored because 9 is an invalid octal
          digit, but "<209.>" would work  properly  since  it  is  a  valid
          decimal number.  

          Also  note  that  when you list a UCL+ symbol definition that in-
          cludes non-printing characters, it displays  their  octal  codes.
          For   instance,  the  escape  character  lists  as  "<033>",  not
          "<027.>".  


          8.4  Running UCL+ Directly 

          You  can  also define (or erase) symbols by running UCL+ directly
          and proceeding as described  above  in  response  to  the  "UCL>"
          prompt.   There  is one significant difference, however:  you can
          include almost any character that you wish in a symbol definition
          (upper/lower case, escape, etc.) as long as RT-11 does not inter-
          cept it for its own purposes (you couldn't use control-O, for ex-
          ample).   In  some  cases,  this  is  an  easier  way  to enter a
          "special" character than the method  described  in  the  previous
          section  (8.3).   This  is  particularly true if you are using an
          earlier version of RT-11 that does not allow the entry  of  lower
          case characters at the monitor level.  

          For  instance,  suppose you wanted to define a symbol to invoke a
          frequently used command file named CLENUP.COM.  Defining the sym-
          bol  from  the UCL+ prompt prevents RT-11 from attempting to pro-
          cess the "@" character.  The dialogue might look  something  like
          the following:  


          UCL+ -- User Command Linkage Program - V08.02a            Page 34
                  Symbols


                    .R UCL
                    UCL> clenup==$@sy:clenup
                    UCL> <ctrl/C>


          The applications notes, particularly the section on defining sym-
          bols that invoke command files and  IND  control  files  (section
          15.1)  and  the  discussion  of  command  line factoring (section
          15.9), contain further examples of when it is useful to run  UCL+
          directly.  


          8.5  Advanced Techniques 

          This  section  contains a description of the "quoting", "argument
          parsing", and "default string" features of UCL+.  The  first  two
          were  added  to UCL+ beginning with V07.50;  the last appeared in
          V07.55.  Support  for  nested  default  strings  was  added  with
          V08.01.   These features are very useful, but they should be used
          with a little care and forethought.  In particular, it is  impor-
          tant to understand how they work (and, perhaps, experiment a bit)
          when defining UCL+ symbols that have nested expansions.  


          8.5.1  Using  The  Quote  Character ("|")  - Quoting is primarily
          used to force  UCL+  to  treat  an  operator  (the  "^"  and  "\"
          characters,  for  example)  as normal text.  This is done by pre-
          ceeding the character to be quoted by the "|" operator.  The most
          common application is to allow characters to be displayed as part
          of a text string that would normally be interpreted as operators.
          For example, the symbol definition:  

                    EXAMPL==_D "|\" 

          Typing EXAMPL would print a "\" at the console.  

          As  a more useful illustration, suppose you wanted to send a line
          of ReGIS graphics instructions to a VT241 (to change  the  screen
          colors,  perhaps).   You will need to preceed the graphics output
          with the text "<esc>Pp" and follow it with "<esc>\" ("<esc>"  in-
          dicates  the  escape  character).   Under TSX-Plus, the following
          symbol definition will do the trick (note the use  of  the  quote
          character to display the "\").  

                    regis==disp "<esc>Pp"\disp "^"\disp "<esc>|\" 

          An  alternate  method  is  to enter the octal code for the escape
          character rather than typing it in directly (escape=33  octal  or
          27 decimal):  

                    regis==disp "<33>Pp"\disp "^"\disp "<33>|\" 


          UCL+ -- User Command Linkage Program - V08.02a            Page 35
                  Symbols


          Refer to section 15.9 of the "Application Notes" for a discussion
          on implementing this symbol under RT-11.  

          It  is  good  policy, by the way, to use the quote character only
          when it is required.  

          The  other thing to watch out for is nested command expansions (a
          symbol defined in terms of another symbol  defined  in  terms  of
          another...).   Consider,  for  example, the problem of defining a
          symbol to display the quote character itself.  The actual  symbol
          definition is 

                    EXAMPL==_D "||||" 

          Why  four  quote  characters?  Because this definition results in               ____
          two "quoting scans":  once when the EXAMPL  symbol  is  processed
          and  expanded, and once when the resultant D (DISPLAY) command is
          scanned.  In other words, the keyboard command to print a "|" is 

                    DISPLAY "||" 

          In order to define a symbol whose expansion is the above command,
          you must quote both  quotes!   (Typing  DISPLAY  "|"  prints  the
          second quotation mark, not a "|" -- think about it.) 

          Most  situations  are not as messy as this one.  The best rule of
          thumb is to "work from the bottom up." 


          8.5.2  Argument  String Parsing ("^n")  - Argument string parsing
          allows you to extend the function of the "^" operator.  UCL+  can
          break  up the "argument part" of a command string into as many as
          nine sub-strings.  These sub-strings are specified  by  following
          the "^" operator with a number from "1" to "9." UCL+ assumes that
          the sub-strings are separated by spaces.  For example, the phrase
          "this  is  a test" consists of four sub-strings.  As a simple il-
          lustration of how this works in practice, consider the  following
          symbol definition.  

                    EXAMPL==_D "^2 ^1" 

          If you type 

                    EXAMPL YOU THERE 

          UCL+ will, in turn, display 

                    THERE YOU 

          A more useful example is PMOVE -- a symbol for "moving" protected
          files:  


          UCL+ -- User Command Linkage Program - V08.02a            Page 36
                  Symbols


                    PMOVE==UNPRO/SYS ^1\COP/SYS/DEL/PROT ^ 

          This  command  will  copy  a  protected  file  from  one place to
          another, and then delete the original copy of the file.   By  the
          way,  once you have PMOVE defined, you can define a sneaky symbol
          that deletes protected files:  

                    PDELET==_PMOVE ^ NL:  

          The  combination "^0" has a special meaning.  This construct will
          supply the number of sub-strings (up to a maximum of  nine)  that
          occur  within a given argument string.  For example, consider the
          following symbol definition:  

                              EXAMPL==_D ""^" HAS ^0 WORDS IN IT" 

          If you type 

                              EXAMPL THIS IS A TEST 

          UCL+ will print 

                              "THIS IS A TEST" HAS 4 WORDS IN IT 

          The  "^0"  construct is most likely to be used when UCL+ builds a
          string to be passed to another program.  This other  program  may
          wish  to  use  the  number  of  sub-strings as a first-line error
          check.  

          Using  argument  parsing is not nearly as tricky as quoting (sec-
          tion 8.5.1, above), but there are a couple  of  basics  that  you
          must keep in mind.  

                o  The  "^"  operator,  unmodified  by  a  trailing numeric
                   value, causes the entire argument string, including  em-
                   bedded  spaces,  to  be inserted into the command expan-
                   sion.  An operator of the form "^n" inserts a sub-string
                   without the "framing" spaces;  i.e., the sub-string will
                   never contain blanks.  

                o  Any  construction of the form "^n" is treated as a pars-
                   ing operator.  However, the sequence "^|n" is  not.   In
                   other  words,  in  an instance where you need to disable
                   parsing, quote the "n".  



          8.5.3  Specifying Default Strings  - When you are defining a sym-
          bol, there may be instances where you wish to  supply  a  default
          argument  string  or sub-string.  This default string will be in-
          serted into the command expansion if the operator does not  enter
          an  argument  string.  Default strings are specified by enclosing

          UCL+ -- User Command Linkage Program - V08.02a            Page 37
                  Symbols


          the text in square brackets ("[]") immediately following the  in-
          sertion operator ("^" or "^n" where "n" is a digit from 1 to 9). 

          A  simple  and  useful example of this technique is the "CD" com-
          mand.  Prior to UCL+ V07.55, CD was a hard-wired command  because
          it was too complex to define as a symbol.  If you typed just "CD"
          with no argument, it expanded into the RT-11 command string  "AS-
          SIGN  SY  DK."  If you included the name of a device, it produced
          "ASSIGN device DK" (e.g., CD DY0 became ASSIGN DY0 DK).  This can
          be  a  very  handy command if, for example, you frequently bounce
          around between a number of logical devices.  

          By  taking advantage of the "default string" feature of UCL+, you
          can define the CD command as a symbol:  

                    CD==ASSIGN ^[SY] DK 

          If  you don't specify an argument string, the default string "SY"
          automatically will be inserted.  Thus, "CD"  becomes  "ASSIGN  SY
          DK", and "CD FOO" expands as "ASSIGN FOO DK." 

          Default  strings  can  also  be used in conjunction with argument
          parsing.  The following example defines an  "RNO"  command  which
          invokes the RUNOFF program:  

                    RNO==R RUNOFF\^2[LP:]=^1\<003> 

          If  you  type  "RNO SCHMOO", RUNOFF processes file SCHMOO.RNO and
          directs output to the printer (LP: is the default output specifi-
          cation).  I.e., you get the following command expansion:  

                    R RUNOFF
                    LP:=SCHMOO
                    <ctrl/C>

          If  you  supply  an  output  spec, it overrides the default text.
          Thus, "RNO SCHMOO TEMP.TXT becomes:  

                    R RUNOFF
                    TEMP.TXT=SCHMOO
                    <ctrl/C>

          You  may  also  nest  default  strings.  For example, suppose you
          didn't want the above RNO command to default to LP as the  output
          device.   Instead, you want it to produce an output DOC file with
          the same name as the input RNO file.   The  following  definition
          will do the trick:  

                    RNO==R RUNOFF\^2[^1]=^1\<003> 

          The  "^2[^1]"  construction  tells UCL+ to use the first argument
          sub-string if a second sub-string is not specified.  Now, if  you

          UCL+ -- User Command Linkage Program - V08.02a            Page 38
                  Symbols


          type "RNO SCHMOO", you will get 

                    R RUNOFF
                    SCHMOO=SCHMOO
                    <ctrl/C>

          If  you  do  specify  an output file explicitly, then the default
          will be overridden.  If you type "RNO SCHMOO TEMP.TXT",  the  ex-
          pansion will be exactly the same as in the earlier example.  

          There  are  a few points to keep in mind when you use the default
          string facility:  

                o  The  default  text is "sticky." Once the text for an in-
                   sertion operator has been  defined,  it  stays  defined.
                   Thus, defining something like 

                        ZORCH==_D "^1[MY] ^1[TEXT]" 

                   is  a  waste  of  typing.  UCL+ scans symbol definitions
                   from left to right, and it will always pick up, and use,
                   the  default  text  "MY";  "TEXT" will never be used.  A
                   specification such as "^1[^2]" is a waste  of  time  for
                   similar reasons.  

                o  Nested defaults only make sense when they are applied to
                   sub-strings.  For example, "^[^1]"  is  pointless  since
                   the  default  would never be used.  The only logical ex-
                   ception is "^[^0]", and I saw no point in adding several
                   lines of code to handle this special case.  Use "^1[^0]"
                   instead.  

                o  UCL+  will  interpret  the  default  string construction
                   "[^]" as "[^1]".  

                o  Any  default specification other than "[^n]", where n is
                   a value from 0 through 9, will be treated as plain text. 


          UCL+ -- User Command Linkage Program - V08.02a            Page 39
                  "Hard-Wired" Commands


          9.0  "HARD-WIRED" COMMANDS 

          The following is a brief description of the commands "hard-wired"
          into UCL+.  These are the commands which support the various UCL+
          functional goodies.  

          Note that, as with RT-11 commands, UCL+ commands and symbols need
          not be typed in their entirety to be recognized.  You  need  only
          type enough characters to make a command unambiguous (and to keep
          it from being mistaken as an RT-11 command).  For example,  "LIST
          COMMANDS" can be abbreviated as "LIS CO" ("LI CO" would be inter-
          preted by RT-11 as a "LINK" command).  

          The  commands are listed in alphabetical order.  Underlining with
          "====" is used to highlight the command itself.   Optional  modi-
          fiers,  switches,  and  so forth, are enclosed in square brackets
          ("[]") and these may be nested (for example,  [["]prompt-text["]]
          indicates  that the quotes are optional as well as the entire ar-
          gument).  

          UCL+ -- User Command Linkage Program - V08.02a            Page 40
                  "Hard-Wired" Commands


          9.1  CHAIN Command

          [NO]CHAIN [file-spec]
              =====

          "Set Up Exit-On-Bad-Command Chain" 

          The  CHAIN  command  allows  you to specify a program for UCL+ to
          chain to if UCL+ is unable to interpret  a  given  command.   The
          original command string is passed to the specified program in the
          same form and in the same fashion that the string  was  given  to
          UCL+.   Issuing  a CHAIN command with no argument restores or re-
          tains the most recent CHAIN file specification.   Note  that  the
          CHAIN  command will also disable UCI_MODE if it is in effect (see
          also section 9.11).  Note also that  CHAINing  is  disabled  when
          UCL+ is running as a UCF.  

          NOCHAIN disables chaining.  

          Examples:

                NOCHAIN
                CHAIN SY:BADWRD.SAV

          UCL+ -- User Command Linkage Program - V08.02a            Page 41
                  "Hard-Wired" Commands


          9.2  DISPLAY Command

          DISPLAY[/switches] command-string
          =======

          or

          DISPLAY "string["]
          =======

          "Display Command Expansion or String"

          The  DISPLAY  command  prints the expansion of the specified UCL+
          command or symbol or, if you enclose the argument with  quotation
          marks, the indicated string is simply printed as is followed by a
          carriage-return/line-feed.  If the trailing quote is omitted,  no
          carriage  control  is  appended (this is the preferred method for
          sending escape sequences).  Output can be directed to the console
          (the default), the printer, or some other specified device/file. 


          Switches:  

          /EXECUTE        prints  the expanded command and then executes it
                          (not valid if DISPLAYing a string).  

          /NOEXECUTE      suppresses command execution (default).  

          /FORM0          allows  the  printer handler to do a formfeed be-
                          fore the first page of output (default;   has  no
                          effect unless SET LP FORM0 command is in effect) 

          /NOFORM0        prevents  the  printer  handler  from executing a
                          formfeed before the first page of output  (recom-
                          mended if you are sending escape sequences to the
                          printer) 

          /PRINTER        directs output to the printer (device LP:).  

          /OUTPUT:file-spec  directs output to the specified device/file.  

          /TERMINAL       directs output to the console (default).  

          Note  that  the  DISPLAY  command is only valid for commands that
          cause a command expansion to be passed to the  keyboard  monitor.
          It  also  does  not work across a CHAIN.  Attempting to DISPLAY a
          "non-expandable" command will cause a "?UCL-E-Invalid DISPLAY ar-
          gument" error message to be issued.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 42
                  "Hard-Wired" Commands


          Examples:

                DISPLAY CD DL0
                DISPLAY/EXECUTE WORD4
                DISPLAY "HERE ARE TWO BEEPS<7><7>"
                DISPLAY/PRINTER "LINE OF TEXT"

          UCL+ -- User Command Linkage Program - V08.02a            Page 43
                  "Hard-Wired" Commands


          9.3  ERASE Command

          ERASE[/switches] symbol1[,symbol2,...]
          =====

          "Erase Symbol(s)"

          The  ERASE  command allows you to delete a symbol or symbols that
          have been previously defined.  If you specify the  entire  symbol
          name,  it  is  deleted  with no verification prompt.  If you only
          type enough of the name to be unambiguous, you will get  an  "Are
          You Sure?" prompt.  

          The command "ERASE *" will delete all of the symbols.  


          Switches:  

          /NOQUERY   omits verification prompt 

          /QUERY     ask  for  operator  verification  (default  if ERASE *
                     used) 

          Examples:

                ERASE ZOOT,FINSTER,WALD
                ERASE *

          UCL+ -- User Command Linkage Program - V08.02a            Page 44
                  "Hard-Wired" Commands


          9.4  LIST Command

          LIST[/switches] [thing1[,thing2,...]]
          ====

          or

          LIST/INDIVIDUAL [symbol-spec1[,symbol-spec2,...]]
          ====

          "List Current Commands/Symbols/Attributes"

          The  LIST  command lists the "hard-wired" commands, currently de-
          fined symbols, CHAIN  assignment/status,  run-by-name  path,  and
          present  release/version to the specified device or file.  If you
          type a LIST command with no arguments, the  symbols  are  listed.
          If  you  omit the output specification, output is directed to the
          console.  

          The /INDIVIDUAL switch allows you to list a single symbol defini-
          tion or a specific subset of the  symbol  definitions.   Wildcard
          characters ("*" and "%") can be used to specify the symbols to be
          listed.  Wildcards work in much the same way that they do in  the
          RT-11  DIRECTORY  command.   E.g., the argument "A*" specifys all
          symbols  whose  name  begins  with  "A";   "A%"  asks   for   all
          two-character names beginning with "A".  

          LIST/INDIVIDUAL does not display the "Current symbols:" header or
          the summary text issued by LIST SYMBOLS.  This is not a bug;   it
          is  a  deliberate  feature.  The intent is to allow you to employ
          the /OUT switch to create subset journal files.  For example, 

                    LIST/I/OUT:MYSYMS.UCJ * 

          would  create  a legitimate UCL+ journal file containing only the
          current symbol definitions.  


          Switches:  

          /FORM0          allows  the  printer handler to do a formfeed be-
                          fore the first page of output (default;   has  no
                          effect unless SET LP FORM0 command is in effect) 

          /INDIVIDUAL     allows the listing of a single symbol or a subset
                          of the symbol definitions;  wildcards can be used
                          in the symbol specification 

          /NOFORM0        prevents  the  printer  handler  from executing a
                          formfeed before the first page of output 

          /OUTPUT:file-spec  sends output to the specified device/file 

          UCL+ -- User Command Linkage Program - V08.02a            Page 45
                  "Hard-Wired" Commands



          /PRINTER        sends output to the printer (LP:) 

          /TERMINAL       sends output to the console (default) 


          Arguments:  

          ALL        list  commands,  symbols,  chain  data, path list, and
                     version.  ("LIST *" has the same effect) 

          CHAIN      list  the  program  to chain to if a command cannot be
                     identified 

          COMMANDS   list the "hard-wired" commands 

          PATH       list the current run-by-name path list 

          SUMMARY    list  the  number of symbols currently defined and the
                     number of entries remaining for new definitions 

          SYMBOLS    list the current symbol definitions (default) 

          VERSION    list the program name and version 


                                        NOTE

               If   you   list  a  symbol  whose  definition  contains
               non-printing characters (an escape character, for exam-
               ple), UCL+ will indicate their presence by printing the
               octal  code  for  each  character  enclosed  in   angle
               brackets.   E.g.,  the "CLS" example in section 8.4 in-
               cludes escape characters (escape=33 octal).   It  would
               list as 

                         CLS   ==_d "<033>[H<033>[J 



          Examples:

                LIST
                LIST CHAIN,PATH
                LIST/PRINTER *
                LIST/INDIVIDUAL A*,B%%%%
                LIST/INDIVIDUAL FOO

          UCL+ -- User Command Linkage Program - V08.02a            Page 46
                  "Hard-Wired" Commands


          9.5  PASS_ON Command

          PASS_ON[/TO:program-name] command-string
          =======

          "Pass On Command To Next (or another) Program"

          This  command  tells UCL+ to pass the specified command-string on
          to the program that you specified via the CHAIN command.  If  you
          specify a "program-name", then the command is passed to this pro-
          gram instead.  If CHAINing is not in effect, and  you  failed  to
          specify  a  program  to  chain to, you get your hand slapped with
          "?UCL-E-No CHAIN in effect".  

          Note that the command string is passed "UCL-style" (byte count at
          location 510, string starting at 512) not "run-by-name" style.  


          /TO:program-name   causes  the command-string to be passed to the
                             specified program 

          Examples:

                PASS_ON LIST
                PASS_ON/TO:BADWRD NUTS==_D "NUTS TO YOU TOO"

          UCL+ -- User Command Linkage Program - V08.02a            Page 47
                  "Hard-Wired" Commands


          9.6  PATH Command

          [NO]PATH  [device1[,device2,...]]
              ====

          "Set Up 'Run-by-name' Search Path"

          If  UCL+  does  not "know" a given command, it follows the device
          list set up with the PATH command in attempting a  "run-by-name".
          It uses DK: by default.  When you enter a new device list, it re-
          places the old one.  The limit is about 20 device mnemonics.   It
          is not necessary to include the trailing colon when you specify a
          device;  "DL0:" and "DL0" are interpreted in the same way.  

          The  NOPATH  command disables the "run-by-name" function.  If you
          have previously issued a NOPATH command, typing the PATH  command
          by itself (no arguments) restores the old search path.  

          Examples:

                PATH DK,DL0,DL1
                NOPATH
                PATH DU0:,DU1:

          UCL+ -- User Command Linkage Program - V08.02a            Page 48
                  "Hard-Wired" Commands


          9.7  PROMPT Command

          PROMPT [["]prompt-text["]]
          ======

          "Change Prompt String"

          The PROMPT command is used to change the UCL+ input prompt.  This
          command is frequently employed when UCL+ is being  used  in  "UCI
          mode".  The replacement prompt text may optionally be enclosed in
          quotes.  If you issue the PROMPT command with  no  argument,  the
          default prompt ("UCL> ") is restored.  

          Note  that  recent versions of TSX-Plus implement a monitor level
          PROMPT command that can interfere with the UCL+  PROMPT  command.
          Section 15.13 discusses this in more detail.  

          Examples:

                PROMPT UCLXM>
                PROMPT "TSXUCL> "

          UCL+ -- User Command Linkage Program - V08.02a            Page 49
                  "Hard-Wired" Commands


          9.8  RECALL Command

          RECALL[/switches]  file-spec
          ======

          "Recall Symbol Definition and Status Tables"

          Recalls (loads) the symbol definition and status area from a file
          that has previously been created with the STORE  command.   (Also
          works with XD files.) The default device is DK:.  The default ex-
          tension is .UCL (i.e., DK:filnam.UCL where "filnam" is  the  file
          name you specify) in binary mode, and .UCJ if the /JOURNAL switch
          is used.  


                                        NOTE

               Beginning  with  RT-11 V5.4C (extended memory monitor),
               and TSX-Plus V6.3, the single-line editor implements  a
               RECALL  command as a SET option.  If this functionality
               is enabled, it preempts the UCL+ RECALL  command.   See
               the  application notes, section 15.12, for a discussion
               of how to work around this problem.  



          Switches:  

          /BINARY    this is the default;  loads a file created as a binary
                     image of the UCL+ symbol/status area 

          /JOURNAL   loads  a  "journal" file;  echos the input to the con-
                     sole if /NOQUIET is in effect 

          /NOQUIET   allows echo of commands to console when doing /JOURNAL
                     input;  use this switch with  caution,  especially  if
                     commands may include console escape sequences 

          /QUIET     this is the default;  suppresses echo of commands when
                     doing /JOURNAL input;   invalid  with  /BINARY;   also
                     suppresses "warning level" messages 

          Examples:

                RECALL SY:UCLXM
                RECALL/JOURNAL BADWRD

          UCL+ -- User Command Linkage Program - V08.02a            Page 50
                  "Hard-Wired" Commands


          9.9  RELOAD command

          RELOAD
          ======

          "Reload The UCL+ Global Region"

          When you are using the special XM version of UCL+, almost the en-
          tire program is permanently resident in a global  region  in  ex-
          tended  memory.   The  RELOAD command allows you to force UCL+ to
          reload this memory region from the copy of the UCL+ program  that
          you are currently running.  

          The RELOAD command always forces UCL+ to run;  it does not return
          to the monitor automatically.  This occurs even if you issue  the
          RELOAD command at the monitor level.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 51
                  "Hard-Wired" Commands


          9.10  STORE Command

          STORE[/switches]  file-spec
          =====

          "Store Current Symbol Definition and Status Tables"

          The  STORE  command causes the symbol/status blocks to be written
          to a specified file.  The default device is DK:.  The default ex-
          tension  is  .UCL (i.e., DK:filnam.UCL where "filnam" is the file
          name you specify) in binary mode, and .UCJ if the /JOURNAL switch
          is used.  

          Switches:  

          /BINARY    this  is the default;  stores a file as a binary image
                     of the UCL+ symbol/status area 

          /JOURNAL   writes  a  "journal"  file;  the file is stored as the
                     series of commands necessary to recreate  the  present
                     UCL+ configuration;  i.e., as an "editable" text file 

          Examples:

                STORE SY:UCL
                STORE/JOURNAL BADWRD

          UCL+ -- User Command Linkage Program - V08.02a            Page 52
                  "Hard-Wired" Commands


          9.11  UCI_MODE Command

          [NO]UCI_MODE  [["]prompt-text["]]
              ========

          "Switch 'UCI Mode' On/Off"

          The  UCI_MODE  command  is  employed  to set up UCL+ for use as a
          "User Command Interface" (UCI).  TSX-Plus provides a facility for
          designating UCIs.  Typically, a UCI is used to process user input
          either prior to, or  instead  of,  the  normal  keyboard  monitor
          (KMON).  

          Issuing a UCI_MODE command has the following effect on UCL+:  

                o  CHAINing  is  disabled.   Non-UCL+  command  strings are
                   passed to KMON for execution.  

                o  If specified, the "prompt-text" replaces the normal UCL+
                   line prompt;  if  no  "prompt-text"  is  specified,  the
                   default  prompt  ("UCL> ")  is assumed (same effect as a
                   PROMPT command).  

                o  The  names of the hard-wired commands are changed by the
                   addition of a "prefix character".  Unless you reassemble
                   UCL+  to change or eliminate it (see section 15.6), this
                   character is a period (".").   Thus,  for  example,  the
                   LIST command becomes ".LIST".  

          NOUCI_MODE acts as follows:  

                o  The  CHAINing  condition in effect prior to the UCI_MODE
                   command is restored.  

                o  If  no prompt-text is specified, the default UCL+ prompt
                   is restored ("UCL> ").  

                o  The normal hard-wired command names are restored.  


          Examples:

                UCI_MODE "UKMON> "
                NOUCI_MODE

          UCL+ -- User Command Linkage Program - V08.02a            Page 53
                  CI Handler


          10.0  CI HANDLER 

          This "handleroid" allows you to turn the  various  RT-11  Command
          Line  Interpreters  (CLIs) on or off using SET commands.  It will
          also show which CLIs are enabled.   There  are  four  CLIs:   UCF
          (User  Commands  First),  DCL  (Digital  Command  Language),  CCL
          (Concise Command  Language),  and  UCL  (User  Command  Linkage).
          Refer to the RT-11 documentation for an explanation of each.  The
          possible SET commands for the CI (Command Interpreter) handleroid
          are:  

               SET CI [NO]UCF  --  turn UCF on/off
               SET CI [NO]DCL  --  turn DCL on/off
               SET CI [NO]CCL  --  turn CCL on/off
               SET CI [NO]UCL  --  turn UCL on/off
               SET CI HELP     --  display SET commands
               SET CI RESET    --  same as SET CI NOUCF,DCL,CCL,UCL
               SET CI SHOW     --  display the active CLIs

          By  default,  RT-11  has  all  CLIs enabled except UCF.  In other
          words, the normal situation is equivalent to 

                    SET CI NOUCF,DCL,CCL,UCL 

          Thus,  if  you  issued  a  SET CI SHOW command under an unaltered
          monitor, CI would report 

                    ?CI-I-CLIs enabled: DCL CCL UCL 

          Note  that SET CI RESET restores/insures the above default condi-
          tion.  


                                     WARNING!!!

               Turning  off both DCL and CCL effectively turns off the
               monitor.  



          It  is  not  possible to INSTALL CI.  This is because CI contains
          only SET code.  As there is no executable handler code, there  is
          no  reason  why CI should be installable -- it would just waste a
          device slot in the monitor tables that could be  used  for  some-
          thing  else.  The monitor will execute the SET options as long as
          CI has the right name  and  resides  on  SY:.   Thus,  for  RT-11
          non-extended  memory  monitors, the file should be SY:CI.SYS.  If
          you are going to use it under a monitor with exended memory  sup-
          port, make a copy named SY:CIX.SYS.  Under RTEM, it should reside
          in the "mark zone" as SY:CIM.SYS.  



          UCL+ -- User Command Linkage Program - V08.02a            Page 54
                  CI Handler


                                        NOTE

               CI  will not run under versions of RT-11 prior to V5.2;
               it will not work with TSX-Plus either.  Also, beginning
               with V5.6, RT-11 implemented a SET CLI command and mod-
               ifications to the appropriate  utilities  which  essen-
               tially  duplicate  the functionality of the CI handler.
               However, CI will still work properly under these  later
               monitors.  




                                 NOTE TO RTEM USERS

               Starting  with  V2.1, RTEM uses the UCF facility to im-
               plement additional monitor commands  and  options  that
               are  specific  to the RTEM environment.  The CI handler
               automatically adjusts to this requirement.  Under RTEM,
               SET  CI  RESET is equivalent to SET CI UCF,DCL,CCL,UCL.
               The text displayed by SET CI  HELP  will  reflect  this
               difference also.  



          UCL+ -- User Command Linkage Program - V08.02a            Page 55
                  Informational Messages


          11.0  INFORMATIONAL MESSAGES 

          Certain  UCL+ operations trigger "informational" messages.  These
          messages, preceeded by "?UCL-I-", are typically used  to  provide
          verification  that a particular action has been taken in response
          to a command.  They are not error messages.  


          ?UCL-I-CHAIN disabled

          Indicates  that  the  NOCHAIN  command  has  been  executed  suc-
          cessfully.  


          ?UCL-I-CHAIN in effect to A....A

          Indicates  that the CHAIN command has been executed successfully.
          "A....A" is the program name.  


          ?UCL-I-Data file not found; creating new one

          Indicates  that the external data (XD) version of UCL+ was unable
          to find its symbol/status file.  A new file is created  and  ini-
          tialized.  


          ?UCL-I-Erased symbol A....A

          Issued  when you erase a symbol via the "null definition" method.
          "A....A" is the symbol name.  


          ?UCL-I-PATH disabled

          Indicates that the NOPATH command has been executed successfully. 


          ?UCL-I-Prompt changed to "A....A"

          Indicates  that  a  PROMPT  command has been issued to change the
          UCL+ command prompt.  "A....A" is the  text  of  the  new  prompt
          string.  


          ?UCL-I-Replaced existing symbol

          Indicates  that  you  have replaced an existing symbol definition
          with another.  



          UCL+ -- User Command Linkage Program - V08.02a            Page 56
                  Informational Messages


          ?UCL-I-"Run-by-name" path: A....A

          Indicates  that  the PATH command has been executed successfully.
          "A....A" is the "run-by-name" path that was  established  by  the
          PATH command.  


          ?UCL-I-UCI_MODE disabled

          Indicates  that  an  explicit  NOUCI_MODE  command  has been suc-
          cessfully issued.  This message is not displayed if a CHAIN  com-
          mand disables a previous UCI_MODE command.  


          ?UCL-I-UCI_MODE enabled

          Indicates that a UCI_MODE command has been successfully issued.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 57
                  Error Messages


          12.0  ERROR MESSAGES 

          The  following  are the error messages for the current UCL+ pack-
          age.  There are three levels of severity.  

          "Warning"  level messages are preceeded with the prefix "?UCL-W-"
          (for example, "?UCL-W-No argument;  CHAIN not enabled"), and they
          indicate  that  the program may have done something that produced
          an erroneous result.  Warning level conditions do not cause  pro-
          gram termination.  

          Most  error  messages  are  preceeded  with  an "E" prefix (e.g.,
          "?UCL-E-Invalid command").  These messages indicate that an error
          of  moderate  severity has occurred.  These might be termed "cor-
          rectable" errors.  If UCL+ has been run directly, this  level  of
          error will cause a return to the program prompt.  

          "Fatal"  messages  are  prefixed  with  "?UCL-F-"  (for  example,
          "?UCL-F-Read error").  A fatal error is a condition that prevents
          the  program  from  running reliably.  When an error of this type
          occurs, UCL+ aborts to the monitor.  


                                        NOTE

               If you are running the XM version of UCL+, some "fatal"
               messages  may  be  issued  through  the  global  region
               loader.    Thus,   if  you  receive  an  error  with  a
               "?UCLGRL-F-" prefix that is not listed as a global  re-
               gion  loader  error,  check the listing of "fatal" mes-
               sages.  



          UCL+ -- User Command Linkage Program - V08.02a            Page 58
                  Error Messages


          12.1  UCL+ "Warning" Messages (?UCL-W-...) 


          No argument; CHAIN not enabled

          You  have  issued  a  CHAIN  command without specifying a program
          name, and no program name had been stored  by  a  previous  CHAIN
          command.  


          Truncating symbol definition to 72 characters

          You  have  used  too many characters to describe a symbol defini-
          tion.  UCL+ stores the new symbol, but truncates  the  definition
          part to 72 characters.  


          Truncating symbol name to 6 characters

          You  have used too many characters in a symbol name.  UCL+ stores
          the new symbol, but truncates the name to 6 characters.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 59
                  Error Messages


          12.2  UCL+ Error Messages (?UCL-E-...) 

          If  you are running under a TSX-Plus V5, or later, monitor, those
          messages    flagged    with    "(*)"    will    result    in    a
          "?KMON-F-Unrecognizable command" error message unless UCL+ is run
          directly.  


          ?UCL-E-Ambiguous command A....A     (*)

          You  have not typed enough characters for UCL+ to determine which
          command or symbol to execute.  "A....A" is the unidentified  com-
          mand.  


          ?UCL-E-Ambiguous switch A....A

          You  have not typed enough characters for UCL+ to determine which
          command switch to use.  "A....A"  is  the  text  of  the  unknown
          switch.  


          ?UCL-E-Ambiguous symbol A....A

          You  issued an ERASE command without specifying enough characters
          for UCL+ to determine which symbol to  erase.   "A....A"  is  the
          name of the ambiguous symbol specification.  


          ?UCL-E-Cannot access LP:

          UCL+  was  unable  to find device LP:, or another job "owns" LP:.
          This error may occur when you use the /PRINT option, and its most
          frequent  cause  is  the failure to make a logical assignment for
          LP:.  


          ?UCL-E-Conflicting switches

          You specified two or more command switches that conflict with one
          another (for example, DISPLAY/TERM/PRINT...).  


          ?UCL-E-File not found A....A

          The  RECALL  command  was unable to find the file that you speci-
          fied.  "A....A" is the file name causing the error.  



          UCL+ -- User Command Linkage Program - V08.02a            Page 60
                  Error Messages


          ?UCL-E-Illegal file name A....A

          You  specified a file name in an invalid format (for example, too
          many characters, or invalid characters).  "A....A" is the errone-
          ous file name.  


          ?UCL-E-Invalid argument A....A

          You issued a hard-wired command with an invalid argument (for ex-
          ample, LIST X).  "A....A" is the text of the argument causing the
          error.  


          ?UCL-E-Invalid command A....A     (*)

          UCL+  was  unable  to recognize the command string (no match with
          the  hard-wired  commands,  no  match  with  the   symbols,   the
          "run-by-name"  search  failed,  and  no  CHAIN  was  in  effect).
          "A....A" is the unknown command string.  


          ?UCL-E-Invalid device

          You  specified  a device that is unknown to the operating system.
          This error occurs with the RECALL or STORE command.  It may  also
          occur if you make an error when you use LIST/OUT:.  


          ?UCL-E-Invalid DISPLAY argument A....A

          You attempted to DISPLAY something that is not DISPLAYable (i.e.,
          the input command does not result in a command expansion;  a LIST
          command,  for example), or you tried to DISPLAY a command or sym-
          bol that does not exist.  "A....A" is the  text  of  the  invalid
          DISPLAY target.  


          ?UCL-E-Invalid or missing option

          You  specified  an  incorrect  option to a command switch, or you
          failed to specify an option value where one was required.  


          ?UCL-E-Invalid switch A....A

          You  specified an illegal command switch.  "A....A" is the switch
          causing the error.  



          UCL+ -- User Command Linkage Program - V08.02a            Page 61
                  Error Messages


          ?UCL-E-Not enough room for file A....A

          The  STORE  command was unable to find enough room for the output
          file (18 blocks are required).  "A....A" is the file name.  


          ?UCL-E-Protected file already exists A....A

          The STORE command was unable to create the output file you speci-
          fied because a protected file of the same  name  already  exists.
          "A....A" is the file name.  


          ?UCL-E-RELOAD invalid while journaling

          The  journal  file that you specified in a RECALL/JOURNAL command
          contained a symbol name that UCL+ interpreted as  a  RELOAD  com-
          mand.   Edit  the  journal file to correct this error and try the
          RECALL command again.  


          ?UCL-E-Symbol definition table full

          You  attempted  to define a new symbol, but UCL+ had no room left
          to store the definition.  


          ?UCL-E-Symbol(s) not found A....A

          The  ERASE  or  LIST/INDIVIDUAL  commands were unable to find the
          name of the symbol that you specified.  "A....A" is  the  unknown
          symbol or symbols.  


          ?UCL-E-UCI_MODE invalid for this monitor

          You  issued  a UCI_MODE command when you were running under RT-11
          or a version of TSX-Plus prior to V5.0.  


          ?UCL-E-Write error A....A

          UCL+  encountered  an  error when it attempted to write data to a
          file.  This error is generated by the STORE command, and  it  im-
          plies  that  the  area  where the ".UCL" file was created is cor-
          rupted.  "A....A" is the name of the  file  in  which  the  error
          occurred.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 62
                  Error Messages


          12.3  UCL+ "Fatal" Messages (?UCL-F-...) 

          ?UCL-F-Cannot access data file

          Under  normal  circumstances,  this error could only occur if you
          have placed the  XD  file  on  a  non-sharable  device,  such  as
          magtape,  and  another  program  already  has  ownership  of this
          device.  It is more likely that this error would be triggered due
          to corruption of the UCL+ program image.  


          ?UCL-F-Cannot create data file

          UCL+  was  unable to create an external data file.  Likely causes
          are a lack of room on  the  disk,  or  a  write-protected  output
          device.  


          ?UCL-F-Data file read error

          An  input error occurred when the XD version of UCL+ attempted to
          load its symbol/status tables from the external data file.  


          ?UCL-F-Data file write error

          An output error occurred when the XD version of UCL+ attempted to
          initialize a newly created external data file.  


          ?UCL-F-Read error A....A

          UCL+  encountered  an error when it attempted to read data from a
          file.  This error is most commonly generated by the  RECALL  com-
          mand.  This may be due to a hard input error, but the usual cause
          is an attempt to RECALL a journal  file  without  specifying  the
          /JOURNAL  switch  to the RECALL command.  "A....A" is the name of
          the file in which the error occurred.  


          ?UCL-F-Write error while updating symbol blocks

          An output error occurred when UCL+ was updating its internal sym-
          bol definition/status tables (or, in the case of the XD  version,
          its  external  data  file).  The UCL+ program file or XD file may
          have been corrupted.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 63
                  Error Messages


          ?UCL-F-Wrong version A....A

          You  tried  to  RECALL  a  symbol definition/status file that was
          created by a version of UCL+ that is too  old.   For  example,  a
          ".UCL"  file created by a V1 UCL+ would be incompatible with a V8
          series program.  "A....A" is the offending file name.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 64
                  Error Messages


          12.4  Global Region Loader Errors (?UCLGRL-F-...) 

          If  you  are running the XM version of UCL+, you may occasionally
          see error messages from the global region loader.  These messages
          are  all  "fatal"  errors  and will be prefixed with "?UCLGRL-F-"
          (for example, "?UCLGRL-F-No room").  

          Also, some UCL+ "fatal" messages may be issued through the global
          region loader.  The only errors documented in  this  section  are
          those  that  are  triggered  by  the global region loader itself.
          Thus, if you receive an error with a "?UCLGRL-F-" prefix that  is
          not  listed as a global region loader error, check the listing of
          "fatal" messages.  


          ?UCLGRL-F-No room

          You  have  insufficient  memory  for  the loader to run.  This is
          highly unlikely under normal circumstances;  the loader never re-
          quires more than 768 words of low memory.  


          ?UCLGRL-F-Not XM monitor

          You  attempted to run the XM version of UCL, but you were not us-
          ing an extended memory monitor.  


          ?UCLGRL-F-PLAS error

          Some  sort  of  memory management related error occurred when the
          loader attempted to create or attach to the global  region.   The
          most likely causes under RT-11 are a shortage of extended memory,
          or an attempt to create too many global regions.  If you are run-
          ning  under a TSX-Plus V6.0 or later monitor, this error can also
          occur if you do not have SYSGBL privilege, or  if  UCL+  has  not
          been INSTALLed with this privilege.  


          ?UCLGRL-F-I/O error

          The  loader encountered a problem when it attempted to access the
          program image on disk.   Possible  causes  include  a  bad  block
          within  the program disk image, or the program storage device may
          be write protected.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 65
                  Error Messages


          12.5  CI Handler Errors (?CI-...) 

          The CI handler generates messages for  two  error  conditions  as
          follows.  


          ?CI-F-Wrong version of RT-11

          You  attempted  you  use  the  CI handler with a version of RT-11
          prior to V5.2.  


          ?CI-W-Disable access to monitor commands/utilities;
                Are you sure?

          You  have  issued a SET command to CI that will result in turning
          off both DCL (Digital Command Language) and CCL (Concise  Command
          Language).   You  are,  in effect, asking to turn off your entire
          RT-11 command interface (except for a few of the UCL+  hard-wired
          commands, assuming that UCF or UCL is still enabled).  In keeping
          with the idea that RT-11 is an "open system", CI  will  go  ahead
          and do this if you respond with "Y" for yes.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 66
                  Examples


          13.0  EXAMPLES 

          Here  are a few examples of some of the symbol definitions that I
          find useful.  They are shown below in the same fashion that  they
          would be listed via a LIST command.  

          $RECAL==_recall
          BIG   ==_d "<033>#3^<033>E<033>#4^"
          BUILD ==delete/info ^.bak\execute/norun ^\delete ^.obj
          CD    ==assign ^[sy] dk
          CLS   ==_d "<033>[H<033>[J
          DBO   ==dir/brief/order:type
          DD    ==dir/order:date/col:1
          EXIT  ==\
          FB    ==boot sy:rt11fb.sys
          FIND  ==ind sy:find
          HLP   ==r uclhlp\^
          INSPEC==edit/inspect
          J     ==show jobs
          MEMORY==show memory
          MOVE  ==cop/sys/del
          NEW   ==dir/new
          NOQUIE==set tt noquiet
          NOWIDE==_d "<033>[?3l<033>[?25h
          PICH10==_d/p/nof "<033>[1w
          PICH16==_d/p/nof "<033>[4w
          QUIET ==set tt quiet
          REBOOT==dup sy:/o/y
          RNO   ==r runoff\^2[^1]=^1\<003>
          SS    ==sh sub
          SUM   ==dir/sum
          ULINE ==_d "<033>[4m^<033>[0m"
          VERSIO==resorc sy:^.sav/v
          VT100 ==set tt scope,tab,nocrlf
          WIDE  ==_d "<033>[?3h<033>[?25h


          These are some definitions that I use on my TSX-Plus system.  

          $RECAL==_recall
          DSP   ==_d
          NOWIND==set window off
          RT11  ==$stop
          SENDME==r transf\^2[^1]/T=^1/S\<003>
          TAKE  ==r transf\^2[^1]=^1/S/T\<003>
          WALKER==_d "You're already logged on, dummy<007>!"
          WINDOW==set window ^[narrow]\set printwindow/dev=ls:/type=la210

          UCL+ -- User Command Linkage Program - V08.02a            Page 67
                  V7 and V8 Release Notes


          14.0  V7 AND V8 RELEASE NOTES 

          This  section  is a journal of the principal changes and enhance-
          ments to UCL+ over the past few years.  It is provided as a  con-
          venience  to those of you who are updating to the current version
          of UCL+, and wish to get an idea of the differences between  this
          version and your current release.  

          Changes to versions prior to V07.55b:  

                o  I changed the release/version designation.  V7C was fol-
                   lowed by V07.04.  

                o  Support has been added to UCL+ to allow it to be used as
                   a User Command Interface (UCI).   This  was  implemented
                   when  the  author discovered that TSX-Plus version 5 was
                   distributed with a UCI facility (heh, heh, heh)...  

                   As  a  consequence,  the  UCI_MODE/NOUCI_MODE and PROMPT
                   commands were added to  allow  UCL+  to  be  dynamically
                   reconfigured  for use as a UCI.  See section 15.5 in the
                   application notes and the description  of  the  UCI_MODE
                   command  (section  9.11) for further information on this
                   feature.  

                o  CHAIN  and  PATH  work  somewhat differently than in V6x
                   versions.  The /RESET switch has been removed.   NOCHAIN
                   and  NOPATH  commands  have  been  added.  The effect of
                   these latter commands is  to  disable  their  respective
                   functions.   A  subsequent CHAIN or PATH command with no
                   argument restores the previous condition.  Note  that  a
                   CHAIN command will turn off UCI_MODE if it is in effect. 

                o  The /ALL switch has been removed from the ERASE command.
                   The equivalent to the old  "ERASE/ALL"  command  is  now
                   "ERASE *".  

                o  The  LIST  command has been expanded.  Either "LIST ALL"
                   or "LIST *" will produce a full listing.  "LIST VERSION"
                   has been added.  

                o  A bug has been fixed concerning the way that UCL+ deter-
                   mines command ambiguity.  Formerly, UCL+ would report  a
                   command  as  ambiguous if it detected an ambiguous match
                   within the hard-wired commands.  UCL+ now  searches  the
                   symbols   as   well   before   returning  an  error.   A
                   non-ambiguous match in the hard-wired command list still
                   takes priority over searching the symbol list.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 68
                  V7 and V8 Release Notes


                o  The  DISPLAY  command has been cleaned up.  UCL+ now re-
                   fuses to DISPLAY "non-expandable" command strings  (most
                   of  the hard-wired commands, insertion or replacement of
                   symbol  definitions,  symbols  defined  in  "chained-to"
                   UCLs).  

                o  A  special  "XM  version" of UCL+ is now included on the
                   distribution kit.  It is intended for use with  monitors
                   having  support  for  global  regions in extended memory
                   (i.e., RT-11 V5.2 or later;  TSX-Plus  V6.0  or  later).
                   Almost all of the "UCLXM" executable code is permanently
                   memory resident.  It is very fast,  and  uses  only  512
                   (decimal) words of low memory.  An additional hard-wired
                   command, "RELOAD", has been added to UCLXM.  

                o  Beginning  with  V07.46,  the  method  that UCL+ uses to
                   search the "run-by-name"  path  list  has  been  changed
                   slightly.  UCL+ no longer exits to the monitor if it en-
                   counters the name of a non-existent device.  Instead, it
                   ignores  the  error,  and  tries  the next device in the
                   list.  

                o  V07.47  added code to "work around" some inconsistencies
                   in the RT-11 spooler.  If,  for  example,  you  issue  a
                   DISPLAY/PRINT/NOFORM0  command  with  spooler  flag page
                   support enabled, you will no longer get an unwanted flag
                   page.   UCL+  also avoids the generation of a gratuitous
                   trailing form feed when the SET LP ENDPAG=n option is in
                   effect.  

                o  V07.50  introduced two new advanced features:  "quoting"
                   and argument parsing.  Quoting allows  you  to  use  the
                   quote  character  ("|")  to  force  UCL+  to  treat  the
                   character immediately following it as  text,  regardless
                   of  any  special  meaning that it might normally have to
                   the UCL+ parser.  Argument parsing makes it possible  to
                   indicate  where a specific fragment of the argument text
                   is to be inserted when building a command string.  

                o  With  V07.53,  the  default  mode for RECALL/JOURNAL has
                   been changed from /NOQUIET to /QUIET.  

          Changes for V07.55b:  

                o  Some minor bugs were fixed in the "run-by-name" and sym-
                   bol format checking algorithms.  

                o  STORE/JOURNAL now outputs NOCHAIN and NOPATH commands if
                   the CHAIN and PATH facilities have been disabled.  


          UCL+ -- User Command Linkage Program - V08.02a            Page 69
                  V7 and V8 Release Notes


                o  The  "^0"  construct was added to allow the insertion of
                   information about how many sub-strings were contained in
                   an argument string.  

                o  Support  was  added  to allow the specification of octal
                   character codes ("<nnn>");  the output of  the  DISPLAY,
                   LIST,  and  STORE/JOURNAL  commands  was changed to this
                   format also.  

                o  The  CI  handler  had  a  bug  which crashed RTEM if the
                   "...Are you sure?" message was triggered;  this has been
                   fixed.  

                o  Provision  was  added  to  allow  the  specification  of
                   default text for the "^" and "^n" insertion operators.  

                o  The CD and RNO hard-wired commands were removed.  CD can
                   be defined as a symbol;  a base-line RNO command can  be
                   specified as a symbol, or the hard-wired version enabled
                   with an assembly conditional.  

          Changes for V07.56:  

                o  The  /INDIVIDUAL  switch  was added to the LIST command.
                   This allows the listing of a  single  symbol  definition
                   or,  through the use of wildcards, a given subset of the
                   currently defined symbols.  

                o  LIST SUMMARY was added which displays the number of sym-
                   bols currently defined and the number of entries  avail-
                   able for additional definitions.  

          Changes for V07.57:  

                o  Informational  messages  were added to verify the action
                   of the [NO]CHAIN and [NO]PATH commands.  

                o  A  warning  message  was  added  to handle the situation
                   where a CHAIN command is issued with no argument, and no
                   program name has previously been established.  

                o  A  bug  was fixed in RECALL/JOURNAL that allowed a blank
                   input line to trigger an attempt to run a program with a
                   null file name if the PATH command was active.  

          Changes for V08.00:  

                o  "External  data" (XD) support was added.  The XD version
                   of UCL+ maintains its symbol/status area in  a  separate
                   data file.  


          UCL+ -- User Command Linkage Program - V08.02a            Page 70
                  V7 and V8 Release Notes


                o  The  XM  and non-XM versions of UCL+ can now RECALL each
                   others context files.  The .UCX extension for XM  binary
                   mode context files was eliminated.  

                o  The  hard-wired  NOSL and SLON commands were eliminated.
                   They are still available as a conditional assembly.  

                o  A bug was fixed in STORE/JOURNAL:  The PROMPT command is
                   listed with the prefix character when UCI_MODE is in ef-
                   fect.  

                o  Error processing was split into "E" and "F" levels.  The
                   latter always forces a hard exit.  

                o  The UCL+ global region loader was modified to compensate
                   for some eccentricities in the TSX-Plus  V6.31  handling
                   of global regions.  

          Changes for V08.01:  

                o  Support  was  added  for "nested" default strings.  This
                   allows one argument sub-string to  act  as  the  default
                   value for another.  

                o  Symbol  definition  processing was modified so that tabs
                   framing the "==" operator would be treated the  same  as
                   spaces.  

          Changes for V08.01c:  

                o  A  bug  was  fixed  in the DISPLAY and PASS_ON commands:
                   Switches with leading blanks caused command arguments to
                   be processed incorrectly.  

          Changes for V08.01d:  

                o  Some minor documentation updates were made.  

          Changes for the latest version (V08.02a):  

                o  Fixed a bug that caused the DISPLAY command to mishandle
                   strings containing character values above 177  octal  if
                   the strings were not being sent to the console.  

                o  Added  support  for  entering character codes in decimal
                   format.  You can now use "<nnn>" for octal  or  "<nnn.>"
                   for decimal values.  

                o  Removed  the  SL$C conditional;  the hard-wired NOSL and
                   SLON commands are no longer available.  


          UCL+ -- User Command Linkage Program - V08.02a            Page 71
                  V7 and V8 Release Notes


                o  Finally  worked around the last reported TSX-Plus global
                   region bug.  This was some sort  of  mysterious  bug  in
                   TSX-Plus that caused the XM version of UCL+ to crash the
                   first time it was run -- sometimes, on some systems.  

                o  Fixed string processing error that occurred when defini-
                   tion was prompted for following null  symbol  definition
                   entry.  

                o  Tested for RT-11 V5.6 and TSX-Plus V6.5 compatibility.  

                o  The documentation was updated.  


          UCL+ -- User Command Linkage Program - V08.02a            Page 72
                  Application Notes


          15.0  APPLICATION NOTES 

          This  section contains an assortment of hints, restrictions, cus-
          tomization patches, and notes for the current version of UCL+.  


          15.1  Executing Command/Control Files "By-Name" 

          UCL+  can  be used to execute indirect command files and IND con-
          trol files "by-name".  In fact, if you set  things  up  properly,
          you  can  ensure that they are executed in the proper context re-
          gardless of whether SET KMON IND is in effect or not.   The  fol-
          lowing examples illustrate the technique.  Note that you must run
          UCL+ directly to define the necessary symbol for a command file. 

          For command files:

                    .R UCL                     _____
                    UCL> zoot==$@sy:zoot                         _______________
                    UCL> <ctrl/C>                         ________

          For control files:

                    .FEEP==IND SY:FEEP                     _________________


          15.2  Sending Escape Sequences To The Printer 

          Starting  with  V6K,  the  LIST  and  DISPLAY  commands include a
          FORM0/NOFORM0 option.  This option allows you to optionally  dis-
          able  the effect of the "SET LP FORM0" command;  i.e., output can
          be directed to the printer without a  preceding  formfeed.   This
          technique is most useful when you wish to send an escape sequence
          to the printer without triggering a  gratuitous  blank  page.   A
          handy  way  to  accomplish this is to define a generalized symbol
          for doing this sort of thing:  

                    .CQWENC==_D/P/NOF "<033>^

          You  can  then  define specific printer-control commands by using
          the general symbol like a "function".   For  example,  to  define
          commands to control the pitch of an LA50/100/210 style printer:  

                    .R UCL
                    UCL> pich10==_cqwenc [1w
                    UCL> pich16==_cqwenc [4w
                    UCL> <ctrl/C>

          UCL+ -- User Command Linkage Program - V08.02a            Page 73
                  Application Notes


          15.3  Moving From UCL+ V6x To UCL+ V8.xx 

          UCL+  V8 will not allow you to RECALL version 6 or earlier series
          .UCL files.  There is a technique, using the RT-11 utility  SIPP,
          that  will  allow  you  to transfer your symbol definitions, etc.
          without reentering them all.  The patch proceeds as follows:  

               1)  Using  SIPP, change the embedded version number at loca-
                   tion 21620 in the old ".UCL" file from 6 to 8.  

               2)  RUN  a  V8.xx  copy  of UCL+ and RECALL the patched sym-
                   bol/status file.  

               3)  Issue a PROMPT command to restore the "UCL>" prompt.  

               4)  Issue a STORE command to write a new ".UCL" file.  

               5)  If  you  need  the CD or RNO commands, implement them by
                   using the techniques described in section 15.11.  

          In  the  example  below,  both the ".UCL" file and the V8 copy of
          UCL.SAV are assumed to be  on  DK:;   "xxxxxx.UCL"  is  your  V6x
          ".UCL"  file.   Note that the SIPP patch is for a V6L file.  Also
          note the use of the /A switch.  

                    .R SIPP                     ______
                    *xxxxxx.UCL/A                     ____________
                    Base?    <ret>                             _____
                    Offset?  21620                             _____

                      Base       Offset      Old  New?
                       000000     021620  006006  \                                                  _

                      Base       Offset      Old  New?
                       000000     021620     006  10                                                  __
                       000000     021621     014  <ctrl/Y>                                                  ________
                    *<ctrl/C>                     ________

                    .RUN UCL                     _______
                    prompt                    ______
                    ?UCL-I-Prompt changed to "UCL> "
                    UCL> recall xxxxxx                         _____________
                    UCL> store xxxxxx                         ____________
                    UCL> <ctrl/C>                         ________

                    .

          Once the above commands have been executed, the resulting V8 copy
          of UCL.SAV will be in the same configuration as your original  V6
          copy.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 74
                  Application Notes


          15.4  Disabling Argument Parsing 

          There may be instances where you do not wish the sequence "^n" to                                              ___
          insert an argument sub-string.  This is most likely to  occur  if
          you  are  converting  an  earlier  version of UCL+ to a V07.50 or
          later version and have a symbol definition that  is  supposed  to
          concatenate  the  argument string with a number.  The solution is
          to use the "|" operator to quote the "n".   The  easiest  way  to
          illustrate  this  is with an example.  Suppose we define a symbol
          named EXAMPL in the following fashion (RT-11 V5.2 syntax):  

                    exampl==_d "^2" 

          If you type 

                    exampl I am R2D 

          UCL+ will display only the word 

                    am 

          because  it  takes the characters "^2" to mean "insert the second
          argument sub-string here." However, if you define EXAMPL as 

                    exampl==_d "^|2" 

          and type 

                    exampl I am R2D 

          UCL+ will then correctly display 

                    I am R2D2 

          Because you have "quoted" the "2", UCL+ interprets the definition
          as "insert the entire argument string ahead of the '2'." 

          UCL+ -- User Command Linkage Program - V08.02a            Page 75
                  Application Notes


          15.5  Hints and Kinks:  UCF, UCI, And SET UCL FIRST 

          If  you  are  using UCL+ as a UCI, command lines are inspected by
          UCL+ before they are processed by the operating system's keyboard               ______
          monitor (KMON).  If you are using UCL+ as UCF or, under TSX-Plus,
          with SET UCL FIRST in effect, KMON collects the command line, but
          it is passed to UCL+ without interpretation.  In any of these in-
          stances, the effect is that UCL+ inspects the command before  the
          monitor  does.   Only if UCL+ does not recognize the command will
          the monitor see the command line in unaltered form.   This  occa-
          sions a couple of "gotchas" that you have to watch out for.  


          15.5.1  Interception  Of Monitor Commands  - Some valid KMON com-
          mands may be trapped prematurely by UCL+.  This situation  occurs
          when there is a conflict between a monitor command or normal com-
          mand abbreviation and a symbol name.  For example, the HELP  com-
          mand  under  TSX-Plus  would  normally  be  invoked as "H", "HE",
          "HEL", or "HELP".  If you wish to avoid a conflict with,  say,  a
          symbol  named  "HELLO",  then it would be necessary to define the
          following symbols:  

                    H==HELP
                    HE==HELP
                    HEL==HELP

          conversely,  the  above  situation allows you to override monitor
          commands with your own.  E.g., 

                    DELETE==_d "The DELETE command is not allowed!" 


          15.5.2  Improper  Expansion  Of  Monitor  Commands  - This second
          gotcha is a little more subtle.  

          Some  monitor  commands  have the same name as the utilities that
          they invoke.  If you are, for example, running as UCF  with  PATH
          in effect, this can cause invalid command expansions.  

          As  an  illustration,  suppose your run-by-name path is "DK:" and
          DK: is currently assigned to SY:.  The  command  "DUMP/TERM  RUB-
          ISH.DAT"  should be passed to KMON undisturbed (assuming that you
          haven't defined your own DUMP command).  However, UCL+ will  spot
          program  DUMP.SAV  on  "DK:",  and  expand  the  command  as "RUN
          DK:DUMP/TERM  RUBISH.DAT".   DUMP   will   see   something   like
          "RUBISH.DAT=/TERM"  and give you what might seem, at the time, to
          be a mysterious error message.  

          I  normally  avoid this problem by disabling the run-by-name path
          (NOPATH command).  If you have a need to retain  the  run-by-name
          search  path,  define  some  symbols  that will cause UCL+ to, in

          UCL+ -- User Command Linkage Program - V08.02a            Page 76
                  Application Notes


          effect, pass your command line to the  monitor  in  an  unaltered
          form.  For the preceeding example, define 

                    DUMP==DUMP


          15.5.3  Single  Key  Commands  - UCL+ is not very picky about the
          characters that you use in symbol names.  If you are  using  UCL+
          as  a  UCI  under  TSX-Plus,  then  you are running UCL+ directly
          whenever you input a command line.  This means that you  can  de-
          fine  some  handy  single-key  symbols  that  the  monitor  would
          strongly disapprove of under normal circumstances.  For example: 

                    \==edit
                    ??????==help

          One user that I know of (Ray Moran) places his VT100 in alternate
          keypad mode (with a UCL+ command, of course!) and  executes  sym-
          bols  whose names correspond to the escape sequences generated by
          the individual keys.  

          If  you  are  using a VT220, or anything with an LK201 style key-
          board.  You have even more keys that you can define!  

          UCL+ -- User Command Linkage Program - V08.02a            Page 77
                  Application Notes


          15.6  UCL+ Assembly Conditionals 

          You  can build a somewhat customized version of UCL+ by modifying
          the conditionals file, UCL.CND, prior to assembly.  

          The prefix conditional, PFX, determines the prefix character used
          by UCL+ when UCI_MODE is in effect.  You can change  this  prefix
          by  changing  the  definition  of PFX from a period (".") to some
          other character.  

          Default strings are delineated by square brackets ("[]").  If you
          wish to use some other set of characters, change the  values  for
          DFPFX  and  DFSFX  to modify, respectively, the prefix and suffix
          character.  

          A  hard-wired  RNO  command can be enabled by defining the condi-
          tional RNO$C:  

                              RNO$C  = 1 

          Edit  this  line  into  the  beginning of file UCL.CND.  RNO is a
          DCL-style command for use with DECUS RUNOFF M02.4.  The  documen-
          tation  for  RNO  can  be  found  in  the source file UCLHWC.MAC.
          Including the RNO command increases  the  size  of  UCL+  by  430
          decimal words.  

          You  can  also remove the UCI_MODE command by setting UCI$C equal
          to 0.  

          Other conditionals are documented in the file UCL.CND.  

          Use  the  command  file UCL.COM to build UCL+, UCLXD.COM to build
          the "external data" variant, and UCLXM.COM to build the  XM  ver-
          sion.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 78
                  Application Notes


          15.7  Changing The RT-11 UCL/UCF Device/File Name 

          The  RT-11 monitor can be modified to run UCL.SAV or UCF.SAV from
          some device other than SY:.  The name of the UCL or  UCF  program
          can  also  be  changed.  To accomplish this, you need to know the
          offsets for some  or  all  of  the  following  locations  in  the
          monitor:  

                o  ..UCLD - UCL device name 

                o  ..UCLF - UCL file name 

                o  ..UCFD - UCF device name 

                o  ..UCFF - UCF file name 

          The  values located at the above offsets are all radix-50 and, as
          you might expect, the file name immediately  follows  the  device
          name.   I.e.,  ..UCLF  is  located  at  ..UCLD+2  and  ..UCFF  at
          ..UCFD+2.  

          If  you  are an orderly person, you can find the values for these
          offsets by inspecting the link map for your monitor.   Note  that
          if  your  monitor version is earlier than V5.2, there will not be
          any ..UCFD/..UCFF values.  

          If you are a somewhat disorderly person (perhaps you are undergo-
          ing TECO withdrawal), you can find ..UCLF and ..UCFF by employing
          the  SIPP  search function and looking for a radix-50 UCL or UCF,
          respectively.  

          In  either case, once you know where these locations are, you can
          use SIPP to patch your monitor to taste.  In the following  exam-
          ple,  the  UCL device is patched from "SY:" to "UCL:".  I usually
          do this because I can then assign some other device to be UCL: in
          my  start-up  command  file  (VM:  is a nice choice).  The labels
          ..UCLD and ..UCLF represent the offsets that were  obtained  from
          the monitor's link map.  

                    .SIPP RT11XM.SYS/A                     _________________
                    Base?    <ret>                             _____
                    Offset?  ..UCLD                             ______

                      Base       Offset      Old  New?
                       000000     ..UCLD  075250  ;R                                                  __
                       000000     ..UCLD   <SY >  ;RUCL                                                  _____
                       000000     ..UCLF   <UCL>  <ctrl/Y>                                                  ________

          If  you  run  more than one type of RT-11 monitor on your system,
          you may wish to use different copies of UCL and/or UCF  depending
          on which monitor is booted.  In the example below, the XM monitor
          is patched to run UCLXM.SAV rather than UCL.SAV.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 79
                  Application Notes



                    .SIPP RT11XM.SYS/A                     _________________
                    Base?    <ret>                             _____
                    Offset?  ..UCLF                             ______

                      Base       Offset      Old  New?
                       000000     ..UCLF  101704  ;R                                                  __
                       000000     ..UCLF   <UCL>  <ret>                                                  _____
                       000000     ..UCLF+2 <   >  ;RXM                                                  ____
                       000000     ..UCLF+4 <SAV>  <ctrl/Y>                                                  ________

          There  is no such thing as a free lunch.  Be aware of the follow-
          ing "patch catches":  

                o  If  you  install either of the above patches, you should
                   use the UCL+ LIST command to obtain a list of  the  cur-
                   rent  symbol definitions even if you are using a version
                   of RT-11 that supports the command "SHOW COMMANDS."  The
                   reason  for  this  is  that RT-11 responds to "SHOW COM-
                   MANDS" by attempting to run SY:UCL.SAV, even though  you
                   have  changed the name of the "UCL" that it uses for all
                   other purposes.  This problem exists in  RT-11  versions
                   as recent as V5.6 -- presumably, it will be fixed sooner
                   or later.  

                o  If  you  change the RT-11 UCL device name, remember that
                   symbol definitions, and such like, will be installed  in
                   the  copy  of UCL+ on the device that you specified.  If
                   that device is VM:, and you have  defined  some  symbols
                   that  you  don't want to lose, use the STORE command, or
                   some other technique, to save  the  UCL+  context  on  a
                   non-volatile device.  


          UCL+ -- User Command Linkage Program - V08.02a            Page 80
                  Application Notes


          15.8  Changing The TSX-Plus UCL/UCI Defaults 

          If you select UCL support when you generate TSX-Plus (if not, why
          are  you  reading  this?),  the  default  UCL  program  name   is
          SY:TSXUCL.SAV  (if you are running V5.0 or later).  Likewise, the
          default name for user-written UCIs is SY:UKMON.SAV.  The  easiest
          way  to change these names is to edit the TSGEN.MAC file prior to
          building TSX-Plus.  These values are not normally modified by the
          user  and,  thus,  will  not  be  found within the "user area" of
          TSGEN.MAC.  If you hunt around  with  the  editor,  however,  you
          should  be able to find them.  For example, if you have V5.1B and
          want to change the UCL default name, you will discover a line  of
          code that should look like 

                    UCLNAM: .RAD50  /SY TSXUCLSAV/ 

          If  you  are  modifying  the UCI default, you will find something
          like 

                    UKMNAM: .RAD50  /SY UKMON SAV/ 

          To change the defaults, edit the rad50 file names prior to assem-
          bling TSGEN.MAC.  For instance, you could edit the value at label
          "UCLNAM:"   to   change   the  UCL  name  from  SY:TSXUCL.SAV  to
          UCL:TSXUCL.SAV.  Further variations on this theme I leave  as  an
          exercise to the user.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 81
                  Application Notes


          15.9  Controlling Command Line Factoring 

          Both RT-11 and TSX-Plus support command line factoring.  However,
          they don't execute it in the same processing sequence.  This  can
          affect the way that you define a symbol that employs factoring as
          part of its definition.  

          For  example, suppose that you wish to define a symbol, "FTN", to
          invoke the FORTRAN compiler in a specialized  fashion  that  com-
          piles  one  or  more files resident on device "FTN:".  If you are
          using TSX-Plus, you can define the symbol at the monitor level:  

                    .FTN==FORT FTN:(^)                     _________________

          However, the example above will not work properly if you are run-
          ning RT-11.  This is because RT-11 expands the factoring prior to
          passing  the  command line to UCL+.  Thus, RT-11 would remove the
          "unnecessary" parentheses in the preceeding  monitor  level  com-
          mand,  and  UCL+  would  see the definition as "FTN==FORT FTN:^".
          The solution, in this case, is to run UCL+ directly:  

                    .R UCL                     _____
                    UCL> ftn==fort ftn:(^)                         _________________
                    UCL> <ctrl/C>                         ________

          The  tendency  of RT-11 to pass "rare" rather than "raw" commands
          to UCL+ can cause more subtle problems also.  

          Suppose, for example, that you wanted to define a command to send
          a line of ReGIS graphics instructions to a VT241  to  change  the
          screen  colors.   You  must  preceed the graphics output with the
          text "<esc>Pp" and follow it with "<esc>\" ("<esc>" indicates the
          escape  character).  At first glance, it would seem that the fol-
          lowing symbol definition sequence would do the  trick  (note  the
          use of the quote operator to display the "\").  

                    .R UCL
                    UCL> regis==disp "<033>Pp"\disp ^\disp "<033>|\"
                    UCL> color==_regis S(M0(AH0L50S100)1( etc...
                    UCL> <ctrl/C>

          Unfortunately, since RT-11 is allowed to "touch" the color speci-
          fication string in the above example, it will strip out  most  of
          the  parentheses, and the COLOR command will not work.  One solu-
          tion is to define the REGIS symbol in such a way that it will run
          UCL+ directly.  (The "<003>" at the end of the "regis" symbol de-
          finition specifies a control-C character.) 

                    .R UCL
                    UCL> regis==r ucl\d "<033>Pp"\d "^"\d "<033>|\"\<003>
                    UCL> color==_regis S(M0(AH0L50S100)1( etc...
                    UCL> <ctrl/C>

          UCL+ -- User Command Linkage Program - V08.02a            Page 82
                  Application Notes


          15.10  Patching UCL+ For RT-11 V5.1 

          When  you  run the UCL+ program, it executes a "context check" to
          determine which environment it  is  running  in.   Unfortunately,
          there  is  a bug in RT-11 V5.1 which sets some extraneous bits in
          the monitor version code.  This causes the non-XM version of UCL+
          to  behave incorrectly when running under V5.1.  If you are using
          UCL+ with RT-11 V5.1, apply  the  following  patch  to  the  file
          UCL.SAV to force UCL+ to assume that it is running under V5.1.  

          Look  at the link map on the UCL+ distribution (UCL.MAP) and find
          the value of the label "FUDGE" (when this document was  prepared,
          the  value  for "FUDGE" was 026356, but you should check the link
          map just to make sure).  Use SIPP to disable the  release/version
          check  in the context routine ("<ret>" denotes a carriage return,
          "<ctrl/Y>" is a control-Y, operator input is underlined):  

                    .SIPP UCL.SAV/A                     ______________
                    Base?    <ret>                             _____
                    Offset?  FUDGE                             _____

                      Base       Offset      Old  New?
                       000000     FUDGE   002002  240                                                  ___
                       000000     FUDGE+2 005067  <ctrl/Y>                                                  ________

          Note  that it is not necessary to apply this type of patch to the
          XM version of UCL+ (UCLXM.SAV) because it will not run under ver-
          sions of RT-11 prior to V5.2.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 83
                  Application Notes


          15.11  Implementing The CD And RNO Commands 

          The  CD and RNO hard-wired commands were dropped from UCL+ begin-
          ning with V07.55.  CD was eliminated  because  the  inclusion  of
          support for default strings in UCL+ made it possible to define CD
          as a symbol.  RNO is no longer included because  almost  everyone
          was  using  it at a base-line level only and, thus, an RNO symbol
          definition would serve just as well in most cases.  

          If  you need the CD command, you can define it as a symbol in the
          following fashion:  

                    CD==ASSIGN ^[SY] DK 

          A base-line RNO symbol can be defined as:  

                    RNO==R RUNOFF\^2[LP:]=^1\<003> 

          There  are,  of  course, several variants on the RNO symbol.  For
          example, if you always emulate form-feeds  with  line-feeds,  you
          can force the /F option into the output specification:  

                    RNO==R RUNOFF\^2[LP:]/F=^1\<003> 

          Both  the CD and RNO symbols are discussed in more detail in sec-
          tion 8.5.3.  

          There  is  also a journal file on the UCL+ distribution kit named
          UCLINI.UCJ that contains symbol definitions for CD and  RNO.   If
          you  wish,  you  can define these symbols by simply RECALLing the
          journal file.  E.g., 

                    RECALL/JOURNAL UCLINI 

          If  you  need the full-fledged, hard-wired RNO command, it can be
          enabled by modifying the UCL+ conditionals file (UCL.CND) and re-
          building UCL+.  Note, however, that the hard-wired RNO command is
          designed to work with DECUS RUNOFF, not the more extensive Bonner
          Labs  version.  The "UCL+ Assembly Conditionals" application note
          (section 15.6) explains how to do this.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 84
                  Application Notes


          15.12  Avoiding Conflicts With The SL RECALL Command 

          Beginning with RT-11 V5.4C, the extended memory  version  of  the
          Single-Line  (SL) Editor implements a RECALL command as a SET op-
          tion.  An SL RECALL command is also  implemented  under  TSX-Plus
          starting  with  V6.3.   Since this command is processed by SL, it
          will always take precedence over the UCL+ RECALL  command.   This
          problem  will  occur in any situation where SL is enabled to pro-
          cess keyboard input, even when UCL+ is run directly.  

          One  solution is to define a symbol that simply expands as a UCL+
          RECALL command in execute-immediate mode.  For example:  

                    RCALL==_RECALL 

          Another  approach  takes  advantage of a peculiarity of the RT-11
          Keyboard Monitor (KMON).  If you  type  $RECALL  at  the  monitor
          prompt,  SL will ignore the command and pass it on to KMON.  KMON
          will, in turn, strip off the leading "$" and pass it on to  UCL+.
          If you decide to use this technique, it's also a good idea to de-
          fine a $RECALL symbol so that everything will  work  consistently
          if you run UCL+ directly.  

          This  same  trick will also work with TSX-Plus (for somewhat dif-
          ferent reasons) as long as you define a  $RECALL  command  within
          UCL+.  

          Note that you must run UCL+ directly to define this symbol:  

                    .R UCL
                    UCL> $recal==_recall
                    UCL> <ctrl/C>

          Finally,  you  can always patch SLX.SYS to change the name of the
          SL RECALL command to something else.  The specifics are  left  as
          an exercise to the reader.  In brief, you must find out where the
          string "RECALL" is stored in the handler (it  will  be  in  ASCIZ
          format)  and  change  it.   If you want to change the SET command
          also, you will need to look in block 0 of SLX.SYS for  two  words
          of RAD50 data that translate to "RECALL." 

          UCL+ -- User Command Linkage Program - V08.02a            Page 85
                  Application Notes


          15.13  Avoiding Conflicts With The TSX-Plus PROMPT Command 

          If you are using UCL+ under a recent version of  TSX-Plus,  there
          is  a  potential conflict between the UCL+ PROMPT command and the
          TSX-Plus PROMPT command.  The simplest solution is  to  run  UCL+
          directly before changing its prompt.  For example:  

                    .r tsxucl                     ________
                    UCL> prompt "tsxucl> "                         _________________
                    ?UCL-I-Prompt changed to "tsxucl> "
                    tsxucl> <ctrl/C>                            ________

          However,  if  you wish to change the UCL+ prompt from the monitor
          level, you need to define a symbol that will  prevent  KMON  from
          intercepting  the  command  prematurely.   The  following example
          shows such a definition for a symbol named "PMT." 

                    pmt==_prompt 

          Note  that  this definition uses "execute immediate" mode to tell
          UCL+ that PMT is defined in terms of a command that UCL+  already
          understands.   This  prevents UCL+ from passing the symbol expan-
          sion back to the monitor.  

          Another  point  to  keep  in mind when you change the UCL+ prompt
          from the monitor level is the importance of  framing  the  prompt
          string  with  quote  characters if you want the prompt to include
          leading or trailing blanks.  For instance, the command 

                    pmt "tsxucl> " 

          specifies  a  trailing  space as part of the UCL+ prompt.  If you
          omit the quotation marks, TSX-Plus will  trim  off  any  trailing
          blanks  before  the command is passed to UCL+.  When you run UCL+
          directly, the quotation marks are not required.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 86
                  Application Notes


          15.14  Controlling External Data (XD) File Initialization 

          Occasionally,  you  may wish to modify the way that the "external
          data"  (XD)  version  of  UCL+  initializes  the  XD  data   file
          (UCLPLS.DAT).   This  is  most  likely if you are installing UCL+
          "locally" under TSX-Plus.  

          Local  installation causes every user, or group of users, to have
          their own private UCL+ set up.  This is accomplished  by  forcing
          the  XD version of UCL+ to maintain a separate copy of UCLPLS.DAT
          for each user.  This file contains the context data  (symbol  de-
          finitions, "run-by-name" path, CHAINing status, etc.) used by the
          UCL+ program.  

          If  the  XD  version of UCL+ cannot find a copy of UCLPLS.DAT, it
          creates one.  The initial configuration specified in this XD file
          is:  

                o  no symbols defined, 

                o  no CHAIN in effect, and 

                o  run-by-name path set equal to "DK:".  

          If  you  need a different initial set-up, you must modify the in-
          ternal configuration of the  UCL+  program.   The  following  il-
          lustrates  the most straightforward approach.  It is assumed that
          you are performing a local installation of the XD version of UCL+
          on a TSX-Plus system (V5.0 or later).  

          First,  you  need to create, and initialize, a copy of UCL+.  You
          will  start  with  a  copy  of  the  "vanilla"  version  of  UCL+
          (UCL.SAV), rather than the XD version (UCLXD.SAV):  

                    .copy ucl.sav sy:tsxucl.sav                      __________________________

          Next, run TSXUCL, and initialize it to the desired base-line UCL+
          configuration for all users on the system.  The following example
          changes the UCL+ prompt, and "pre-defines" the CD and RNO symbols
          by RECALLing them from the UCLINI.UCJ journal file.   (This  file
          is included on the UCL+ distribution kit).  

                    .r tsxucl                      ________
                    UCL> prompt "tsxucl> "                          _________________
                    ?UCL-I-Prompt changed to "tsxucl> " 
                    tsxucl> recall/journal uclini                             _____________________
                    <eof> 
                    tsxucl> <ctrl/C>                             ________

          Since  you  are  performing a local installation, you should also
          establish a specific device for each user,  or  group  of  users,
          that  will contain their individual copy of UCLPLS.DAT.  The best

          UCL+ -- User Command Linkage Program - V08.02a            Page 87
                  Application Notes


          way to do this is to assign the logical  mnemonic  "UCL:"  within
          each user's start up command file.  For example:  

                    MOUNT LD0 DU1:FRED.DSK DK
                       .
                       .
                       .
                    ASSIGN DK UCL

          Finally,  patch  TSXUCL.SAV to enable XD support.  This is accom-
          plished by changing the contents of location SDSBBK from 1 to  0.
          (When this document was prepared, the value of SDSBBK was 032634,
          but you might wish to check the link map, UCL.MAP, just  to  make
          sure.   A  more complete discussion of this patch can be found in
          application note 15.15.) 

                    .sipp tsxucl.sav/a                     _________________
                    Base?    <ret>                             _____
                    Offset?  SDSBBK                             ______

                      Base       Offset       Old   New?
                       000000     SDSBBK   000001   0                                                    _
                       000000     SDSBBK+2 050162   <ctrl/Y>                                                    ________

          Once  XD  support  is  enabled,  UCL+  will  behave  as  follows:
          Following logon, whenever a user invokes UCL+ it  will  load  its
          symbol/status data from UCL:UCLPLS.DAT.  Any UCL+ context changes
          (defining a new symbol, for example)  are  posted  to  this  file
          also.  If UCLPLS.DAT does not exist, UCL+ will create it, and is-
          sue the message "?UCL-I-Data file not found;  creating new  one".
          If you defined any symbols within TSXUCL.SAV prior to enabling XD
          support, these definitions will show up in each user's UCLPLS.DAT
          when it is created.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 88
                  Application Notes


          15.15  Enabling/Disabling UCL+ External Data (XD) Support 

          External data (XD) support can be enabled or disabled by patching
          a single location in the non-XM version of UCL+.   In  fact,  the
          only difference between the distributed "vanilla" version of UCL+
          (UCL.SAV) and the XD version (UCLXD.SAV) is the contents of  this
          one location.  

          When  XD  support  is  disabled, UCL+ maintains its symbol/status
          data  "internally."  The  symbol  definitions,  CHAIN  and   PATH
          specifications,  and  so  forth,  are stored within the program's
          disk image.  When these context data are changed, the disk  image
          is modified.  

          When  XD  support is enabled, the UCL+ context area is maintained
          in a separate file named UCLPLS.DAT.  This XD file is located  on
          device  UCL:,  if this logical mnemonic is defined on the system.
          If UCL: is undefined, UCL+ looks for it on SY:.  UCL+ will create
          the XD file if it does not exist.  

          To  enable  XD support, use the following SIPP patch.  The string
          "nnnnnn" is the name of the program you are  patching.   "SDSBBK"
          is  the location to be patched.  (The value for SDSBBK was 032634
          when this document was written, but you may wish to  verify  this
          from the link map, UCL.MAP.) 

                    .SIPP nnnnnn.SAV/A                     _________________
                    Base?    <ret>                             _____
                    Offset?  SDSBBK                             ______

                      Base       Offset       Old   New?
                       000000     SDSBBK   000001   0                                                    _
                       000000     SDSBBK+2 050162   <ctrl/Y>                                                    ________

          The  same,  basic  patch  can be used to disable XD support.  The
          only difference is that you place a 1 in location SDSBBK  instead
          of a 0.  

          In  summary,  a  1  in  location SDSBBK disables XD support;  a 0
          turns it on.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 89
                  Application Notes


          15.16  Changing The External Data (XD) Device/File Name 

          The  UCL+  external  data  (XD) file is usually named UCLPLS.DAT.
          When UCL+ is searching for this file, it  looks  on  device  UCL:
          first.  If UCL: does not exist, UCL+ defaults to SY:.  It follows
          the same logic when the XD file  is  created:   If  UCL:  exists,
          UCLPLS.DAT is created there.  If not, the file is created on SY:. 

          If you need to change the XD device or file name, you can do this
          with a SIPP patch.  To change the XD  device,  change  the  RAD50
          contents of location XDDEV.  The file name, also stored in RAD50,
          can be changed by patching the three words starting at XDFIL.  At
          the  time  this  document  was  written,  the value for XDDEV was
          036400, and XDFIL was 036402.  (You can verify this  by  checking
          the link map, UCL.MAP.) Note that XDFIL immediately follows XDDEV
          -- i.e., XDFIL = XDDEV+2.  

          In  the  example  below,  a copy of UCLXD.SAV named MYPROG.SAV is
          patched to change the XD device/file name to SY:MYPROG.DAT.   The
          reason  the  device  mnemonic is changed from UCL: to SY: is that
          this forces MYPROG to keep its XD file on the system device.  

                    .SIPP MYPROG.SAV/A                     _________________
                    Base?    <ret>                             _____
                    Offset?  XDFIL                             _____

                      Base       Offset      Old  New?
                       000000     XDDEV   101704  ;R                                                  __
                       000000     XDDEV    <UCL>  ;RSY                                                  ____
                       000000     XDDEV+2  <UCL>  ;RMYP                                                  _____
                       000000     XDDEV+4  <PLS>  ;RROG                                                  _____
                       000000     XDDEV+6  <DAT>  <ctrl/Y>                                                  ________


          UCL+ -- User Command Linkage Program - V08.02a            Page 90
                  Application Notes


          15.17  Implementing Both Global And Local Symbols Under TSX-Plus 

          It  is  possible to install UCL+ in such a way that each TSX-Plus
          user will have access to both a "local" and a "global" set of UCL
          symbols.  The local symbols are unique to, and maintained by, the
          individual users.  The global symbols are  system-wide,  and  are
          (presumably) maintained by the system manager.  

          TSX-Plus UCL sequencing will work in the normal fashion with this
          addition:  If a symbol is not found in the local set, the  global
          set  will be searched.  Note that this also means that local sym-
          bol definitions will take precedence over global definitions.  

          Here's how you set things up:  

          First,  install a copy of the "vanilla" UCL+ program, UCL.SAV, on
          the system device.  Name it UCLGBL.SAV.  Define all  your  global
          symbols  within this program.  (You'll have to run it directly to
          do this.) You can use the installation instructions  in  sections
          6.1.2 and 6.1.2.1 as a guideline for installing UCLGBL.  However,
          you should give casual users read-only access to SY:UCLGBL.SAV.                                         _________

          Next,  install  an XD version of UCL+, following the general pro-
          cedures decribed in section 15.14.  Prior to enabling XD support,
          initialize  TSXUCL so that it CHAINs to SY:UCLGBL.SAV.  It's also
          a good idea to "pre-define" some sort  of  "list  global"  symbol
          (GLIST  is a possible name) that will make it easy for users look
          at the global symbol definitions.  The following illustrates this
          initialization sequence:  

                    .r tsxucl
                    UCL> prompt "tsxucl> "
                    ?UCL-I-Prompt changed to "tsxucl> "
                    tsxucl> chain sy:uclgbl.sav
                    tsxucl> glist==_pass list
                    tsxucl> <ctrl/C>

          Essentially, what you end up with is two UCL+ programs strung to-
          gether.  TSXUCL maintains, and processes, the user's local symbol
          definitions.  But, if a symbol is invoked that the local UCL does
          not recognize, the global UCL will get a crack at it.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 91
                  Application Notes


          15.18  Eliminating the TSX-Plus UCL Data File (TSXUCL.TSX) 

          Later  versions  of  TSX-Plus  automatically  create  a data file
          (TSXUCL.TSX) for use by the distributed UCL program.  Of  course,
          if  you are using UCL+, this file is of no practical use, and you
          can delete it with no adverse effect once TSX-Plus is booted.  

          There  is  also  a  sneakier  way to get rid of TSXUCL.TSX.  This
          method requires the modification of TSGEN.MAC prior  to  building
          TSX-Plus.  Or, if you are using a recent version of TSX-Plus, you
          can accomplish the same thing with the TSXMOD program.  In either
          case,  you need to modify the file specification at label UCLDAT.
          The file spec will look like this:  

                    UCLDAT: .RAD50  /SY TSXUCLTSX/ 

          Once you have located this file name, change the device spec from
          SY to the null device, NL.  

                    UCLDAT: .RAD50  /NL TSXUCLTSX/ 

          Since  NL  cheerfully accepts I/O requests without actually doing
          anything, TSXUCL.TSX never  gets  created.   At  the  same  time,
          TSX-Plus  seems to be perfectly happy, as long as it's allowed to
          go through the motions of creating the file.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 92
                  Reporting Problems and Suggestions


          16.0  REPORTING PROBLEMS AND SUGGESTIONS 

          I want to know about bugs!  

          I am also interested in suggestions for improving UCL+ as well as
          any interesting applications that you may have found for it.  

          I can be contacted by telephone or paper mail at:  


                    William K. Walker
                    RDB/Alpha Systems
                    P. O. Box 149
                    Alpha, OH  45301-0149
                    (513) 426-7094/0344


          My electronic addresses are:  


                    CompuServe: 71066,24
                      MCI Mail: rdbalpha
                      Internet: rdbalpha@mcimail.com
                                71066.24@compuserve.com
                         Telex: 6503331675 (6503331675 MCI UW)


          If you discover a genuine bug in the current version of UCL+, and
          you are the first to report it, you get a post-paid copy  of  the
          next release -- you can even keep the floppys.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 93
                  Wish List


          17.0  WISH LIST 

          Aside from the usual fiddling about with the internals, I am cur-
          rently thinking about the following additions/changes  to  future
          versions of UCL+:  

                o  a  reasonable way to change the number of characters al-
                   located for symbol names and symbol definitions, and 

                o  a  method  to  change the total number of symbol defini-
                   tions allowed in UCL+.  

          I  do  NOT  intend to implement a "symbol definition editor." Use
          STORE/JOURNAL or LIST/INDIVIDUAL/OUT and edit the output.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 94
                  UCL+ Command and Syntax Summary


          18.0  UCL+ COMMAND AND SYNTAX SUMMARY 



                              SYMBOL DEFINITION SYNTAX                              ________________________

          name==definition

          where "name"       is a six-character symbol name
                "definition" specifies the symbol expansion


                                      OPERATORS                                      _________

             ==        symbol definition

             \         line separation/termination

             ^n[text]  argument insertion
                            if "n" used, insert nth part
                            if "[text]" used, "text" is default string
                               "[^m]" means use mth part as default

             _         "execute-immediate" flag

             <nnn>     insert character whose octal code is "nnn"
             <nnn.>    insert character whose decimal code is "nnn."

             |         quote flag; treat next character as text only


                                "HARD-WIRED" COMMANDS                                _____________________

          CHAIN     Sets up UCL+ exit chaining
          DISPLAY   Displays a string or UCL+ command/symbol expansion
          ERASE     Deletes one or more UCL+ symbols
          LIST      Lists the current UCL+ commands/symbols/status
          PASS_ON   Passes a command string to a program "UCL-style"
          PATH      Sets up the UCL+ "run-by-name" path
          PROMPT    Sets the UCL+ command-line prompt string
          RECALL    Loads symbol definition and status tables
          RELOAD    Reloads a UCL+ global region (XM version only)
          STORE     Saves the UCL+ symbol definition and status tables
          UCI_MODE  Set UCL+ "pass-line-to-KMON" mode (TSX-Plus only)


                                FILE NAME EXTENSIONS                                ____________________

                    .DAT     "External data" symbol/status file
                    .UCJ     Journal mode symbol/status file
                    .UCL     Binary mode symbol/status file

          UCL+ -- User Command Linkage Program - V08.02a            Page 95
                  UCL+ Customization Patch Summary


          19.0  UCL+ CUSTOMIZATION PATCH SUMMARY 

          The  following  is  a list of the UCL+ customization patches men-
          tioned in various places in this  manual.   The  section  numbers
          refer  to  the  primary section of the manual where each patch is
          discussed.  The information in the "Symbol" and  "Value"  columns
          is abstracted from the link map, UCL.MAP.  



          Symbol    Value     Section   Effect          ______    _____     _______   ______

          FUDGE     026356    15.10     Work around RT-11 V5.1 bug

          SDSBBK    032634    15.15     Enable/disable XD support

          XDDEV     036400    15.16     Change XD file default device

          XDFIL     036402    15.16     Change XD file name


          The values listed for these patches were current at the time this
          manual was produced.  However, it  never  hurts  to  double-check
          them against the link map.  

          UCL+ -- User Command Linkage Program - V08.02a            Page 96
                  I N D E X


          20.0  INDEX 

          This is, for now, a partial index;  I will expand it as time per-
          mits.  The emphasis is on the UCL+ commands and major components. 

          This section is intended to serve as a supplement to the table of
          contents.  In many cases the table of contents provides a  suffi-
          cient  level  of detail to locate a particular subject.  In these
          instances, index entries are either omitted or simplified.  

          UCL+ commands appear in upper case.  


          % character 
            see Wildcards 

          * character 
            see Asterisk, embedded and Wildcards 

          == operator 
            see Defining symbols 

          Argument parsing  . . . . . . . . . .   7, 34, 35, 36, 37, 68, 74
          Asterisk, embedded  . . . . . . . . . . . . . . . . . . . .    30

          Bugs 
            Fixed . . . . . . . . . . . . . . . . . . . .    67, 68, 69, 70
            Reporting . . . . . . . . . . . . . . . . . . . . . . . .    92
            RT-11 V5.1 patch  . . . . . . . . . . . . . . . . . . .   2, 82

          CCL . . . . . . . . . . . . . . . . . . . . . . . . . . . .    53
          CD  . . . . . . . . . . . . . . . . . . . . . . .    2, 9, 69, 73
            Defining  . . . . . . . . . . . . . . . . . . . .    37, 83, 86
          CHAIN . . . . . . . . . . . . . . . . .    27, 41, 44, 67, 69, 90
            Description . . . . . . . . . . . . . . . . . . . . . . .    40
            Disabled by UCF . . . . . . . . . . . . . . . . . . . . .    40
            Disabled by UCI_MODE  . . . . . . . . . . . . . . . . . .    52
            Effect on UCI_MODE  . . . . . . . . . . . . . . .    40, 56, 67
            Error message . . . . . . . . . . . . . . . . . . . . . .    58
            Informational message . . . . . . . . . . . . . . . . . .    55
            Invoked via PASS_ON . . . . . . . . . . . . . . . . . . .    46
            Restored by NOUCI_MODE  . . . . . . . . . . . . . . . . .    52
            Showing its status  . . . . . . . . . . . . . . . . . . .    45
          CI handler  . . . . . . . . . . . . . . . . . . . . .    7, 8, 28
            Description . . . . . . . . . . . . . . . . . . . . . . .    53
            Error messages  . . . . . . . . . . . . . . . . . . . . .    65
            Installation  . . . . . . . . . . . . . . . . . . . . . .    24
            RT-11 and TSX-Plus restrictions . . . . . . . . . . . . .    54
            RTEM bug  . . . . . . . . . . . . . . . . . . . . . . . .    69
            RTEM installation . . . . . . . . . . . . . . . . . . . .    26
          Concise Command Language 
            see CCL 

          UCL+ -- User Command Linkage Program - V08.02a            Page 97
                  I N D E X


          DCL . . . . . . . . . . . . . . . . . . . . . . . . . . . .    53
          Default strings . . . . . . . . .    1, 7, 34, 36, 37, 38, 69, 83
            Changing delineators  . . . . . . . . . . . . . . . . . .    77
            Nested  . . . . . . . . . . . . . . . . . . .    34, 37, 38, 70
          Defining symbols 
            (see also "Symbols" section) 
            Examples  . . . . . . . . . . . .    66, 72, 74, 75, 76, 81, 84
          Digital Command Language 
            see DCL 
          DISPLAY . . . . . . . . .   6, 31, 32, 35, 59, 60, 68, 69, 70, 72
            Description . . . . . . . . . . . . . . . . . . . . . . .    41
            Use with TSX-Plus . . . . . . . . . . . . . . . . . . . .    29

          ERASE . . . . . . . . . . . . . . . . . . . . . . . . . .   6, 32
            /ALL removed  . . . . . . . . . . . . . . . . . . . . . .    67
            Description . . . . . . . . . . . . . . . . . . . . . . .    43
            Error messages  . . . . . . . . . . . . . . . . . . .    59, 61
          Execute-immediate mode  . . . . . . . . . . . . . .    31, 32, 84

          Global region . . . . . . . .   7, 13, 14, 15, 16, 17, 50, 64, 68
          Global region loader  . . . . . . . . . . . . . . . . . . .    70
            Error messages  . . . . . . . . . . . . . . . . . . . . .    64

          Installation 
            see "Installation" section 

          LIST  . . . . . . . . .    27, 39, 45, 46, 52, 60, 67, 69, 72, 79
            /INDIVIDUAL . . . . . . . . . . . . . . . .   1, 44, 45, 61, 93
            Description . . . . . . . . . . . . . . . . . . . . . . .    44

          NOCHAIN . . . . . . . . . . . . . . . . . . . . . .    67, 68, 69
            Description . . . . . . . . . . . . . . . . . . . . . . .    40
            Informational message . . . . . . . . . . . . . . . . . .    55
          NOPATH  . . . . . . . . . . . . . . . . . . . .    67, 68, 69, 75
            Description . . . . . . . . . . . . . . . . . . . . . . .    47
            Informational message . . . . . . . . . . . . . . . . . .    55
          NOSL 
            see SLON 
          NOUCI_MODE  . . . . . . . . . . . . . . . . . . . . . . . .    67
            Description . . . . . . . . . . . . . . . . . . . . . . .    52
            Informational message . . . . . . . . . . . . . . . . . .    56

          PASS_ON . . . . . . . . . . . . . . . . . . . . . . . . .   6, 70
            Description . . . . . . . . . . . . . . . . . . . . . . .    46
          PATH  . . . . . . . . . . . . . . . . . . . . .    18, 27, 67, 69
            (see also Run-by-name) 
            Description . . . . . . . . . . . . . . . . . . . . . . .    47
            Informational message . . . . . . . . . . . . . . . . . .    56
            Showing its status  . . . . . . . . . . . . . . . . . . .    45
            Using with UCF  . . . . . . . . . . . . . . . . . . . . .    75
          PROMPT  . . . .    11, 14, 15, 17, 20, 22, 52, 67, 70, 73, 86, 90
            Conflict with TSX-Plus PROMPT . . . . . . . . . . . .    48, 85

          UCL+ -- User Command Linkage Program - V08.02a            Page 98
                  I N D E X


            Description . . . . . . . . . . . . . . . . . . . . . . .    48
            Informational message . . . . . . . . . . . . . . . . . .    55

          Quoting . . . . . . . . . . . . . . . . .   7, 34, 35, 36, 68, 81

          RECALL  . . . . .   6, 10, 11, 12, 13, 14, 16, 18, 19, 21, 22, 27
            /JOURNAL  . . . . . . . . . . . . . . . . . .    61, 68, 69, 86
            Conflict with SL RECALL . . . . . . . . . . . . . . .    49, 84
            Description . . . . . . . . . . . . . . . . . . . . . . .    49
            Error messages  . . . . . . . . . . . . . . .    59, 60, 62, 63
            V6x file recovery . . . . . . . . . . . . . . . . . . . .    73
            V8.xx changes . . . . . . . . . . . . . . . . . . . . . .    70
          RNO . . . . . . . . . . . . . . . . . . . . . . .    2, 9, 69, 73
            Defining  . . . . . . . . . . . . . . . . . .    37, 66, 83, 86
            Hard-wired command  . . . . . . . . . . . . . . . . .    77, 83
          Run-by-name . . . . . . . . .   6, 27, 28, 29, 44, 46, 47, 60, 68
            (see also PATH, NOPATH) 

          SLON  . . . . . . . . . . . . . . . . . . . . . . . . . .   2, 70
          STORE . . . . . . . .    1, 6, 10, 12, 14, 16, 18, 21, 49, 73, 79
            /JOURNAL  . . . . . . . . . . . . . . . .    51, 68, 69, 70, 93
            Description . . . . . . . . . . . . . . . . . . . . . . .    51
            Error messages  . . . . . . . . . . . . . . . . . . .    60, 61
          Symbols 
            see "Symbols" section 

          UCF . . . . . . . . . . . . . . . . . . . . .   5, 27, 29, 53, 65
            Changing RT-11 defaults . . . . . . . . . . . . . . . . .    78
            Command processing  . . . . . . . . . . . . . . . . . . .    28
            Effect on CHAIN . . . . . . . . . . . . . . . . . . . . .    40
            Hints and kinks . . . . . . . . . . . . . . . . . . . . .    75
            UCL.SAV installation  . . . . . . . . . . . . . . . . . .    11
            UCLXD.SAV installation  . . . . . . . . . . . . . . . . .    19
            UCLXM.SAV installation  . . . . . . . . . . . . . . . . .    15
            Under RTEM  . . . . . . . . . . . . . . . . . . . . . . .    54
          UCI . . . . . . . . . . . . . . . . . . . . .    5, 6, 27, 29, 67
            Changing TSX-Plus defaults  . . . . . . . . . . . . . . .    80
            Hints and kinks . . . . . . . . . . . . . . . . . . . . .    75
            UCL.SAV installation  . . . . . . . . . . . . . . . . . .    12
            UCLXD.SAV installation  . . . . . . . . . . . . . . . . .    22
            UCLXM.SAV installation  . . . . . . . . . . . . . . . . .    17
          UCI_MODE  . . . . . . . . . . . . . . . . . . . .   6, 23, 29, 67
            Changing "prefix character" . . . . . . . . . . . . . . .    77
            Description . . . . . . . . . . . . . . . . . . . . . . .    52
            Disabled by CHAIN . . . . . . . . . . . . . . . . . .    40, 67
            Error message . . . . . . . . . . . . . . . . . . . . . .    61
            Informational message . . . . . . . . . . . . . . . . . .    56
            Invokes "prefix character"  . . . . . . . . . . . . . . .    52
            Removing support for  . . . . . . . . . . . . . . . . . .    77
          UCL . . . . . . . . . . . . . . . . . . . . . . . . .   5, 53, 65
            Changing RT-11 defaults . . . . . . . . . . . . . . . . .    78
            Changing TSX-Plus defaults  . . . . . . . . . . . . . . .    80

          UCL+ -- User Command Linkage Program - V08.02a            Page 99
                  I N D E X


            UCL.SAV installation  . . . . . . . . . . . . . . . .    10, 12
            UCLXD.SAV installation  . . . . . . . . . . . . . . .    18, 21
            UCLXM.SAV installation  . . . . . . . . . . . . . . .    14, 16
          User Commands First 
            see UCF 
          User Commands Last 
            see UCL 
          User Command Interface 
            see UCI 

          Wildcards . . . . . . . . . . . . . . . . . . . . . . .    44, 69

          \ operator 
            see Defining symbols 

          ^ operator 
            see Defining symbols, Argument parsing 

          _ operator 
            see Defining symbols, Execute-immediate mode 

          | operator 
            see Defining symbols, Quoting