DDDD   SSSSS  L      IIIII  BBBB 
                     D   D  S      L        I    B   B
                     D   D  SSSSS  L        I    BBBB 
                     D   D      S  L        I    B   B
                     DDDD   SSSSS  LLLLL  IIIII  BBBB 















                               DAVID STAGG

                       Department of Pharmacology
                     Yale University Medical School
                            333 Cedar Street
                           New Haven  Ct 06510

                              203-436-3617


















     DSLIB                                                       Page   2
                                                                30 Oct 80


                              INTRODUCTION                              ____________



     DSLIB is a collection of subroutines for use with RT-11 Fortran.

     SPFILE and SPFILN are intended to make the  selection  of  filenames
     easier particularly by checking for errors in file specification and
     giving warnings for non-existent input files and pre-existent output
     files.   These subroutines will also identify the physical device on
     which the file will be located.  SPFILE allows files to be specified
     with  the  full  RT11 naming conventions.  SPFILN allows files to be
     specified numerically.

     FREEFL is a routine which will find the first non-existent file in a
     sequence of files which are specified numerically.

     GETFIL, FTRAN, FCHECK and ASLOOK are primarily intended to be called
     by  the  previous  subroutines but may be called directly to provide
     information about RT11 files.

     YESCHK is an integer function which will  give  a  simple  numerical
     value  in  response  to a question requiring a 'YES' or 'NO' type of
     answer.

     LNUM and ILNUM  enable  decimal  numbers  to  be  extracted  with  a
     completely free format from a character string.

     RENAME is a routine which simplifies the process of  renaming  files
     from within a Fortran program.

     RFILT performs triangular or trapezoidal filtering of a real array.

     VALDAT aborts with a message if the date has not been entered.


     The subroutines have been compiled for  minimum  program  space  and
     combined into the library DSLIB.
























     DSLIB                                                       Page   3
                                                                30 Oct 80


                            SUBROUTINE SPFILE                            __________ ______



     A routine to simplify the specification of a  filename  by  checking
     for  syntax errors, supplying an actual device name and checking for
     validity if a logical device name is specified and checking for  the
     existence  of  an  input  file  or  the  possible  replacement  of a
     pre-existing output file.


     The call is of the form:

          CALL SPFILE(NAMER,NAMEA,IEXT,MODE,TITLE,IRET)

     where

          NAMER   Is a 4  word  integer  array  which  receives  a  RAD50
          representation of the filename.

          NAMEA   Is a 15 byte array which receives  an  ASCII  character
          representation of the filename.

          IEXT    Is a RAD50 default extension for the filename.

          MODE    Is the mode of the call formed by adding  options  from
          the following list:

                  MODE =1  An output file is required (otherwise an input
                           file is assumed)
                  MODE =2  The existing string in NAMEA will be used  for
                           the filename
                  MODE =4  The routine will continue  to  request  a  new
                           filename   until  an  acceptable  response  is
                           typed.

          TITLE   Is a character  string  printed  by  the  routine  when
          requesting the filename.

          IRET    A parameter returned with the following significance:

                  IRET=-2  The file specified has zero blocks
                  IRET=-1  The file specified does not exist
                  IRET= 0  A non-file structured lookup was specified
                  IRET >0  An existing file of IRET blocks was found


     Unless MODE=2 has been  selected,  the  subroutine  will  request  a
     filename  by printing 'WHAT IS THE <TITLE> FILE NAME ?' and wait for
     a reply.
     If a device name is not specified, the device DK:  will  be  assumed
     and if an extension is not specified <IEXT> will be used.  If MODE=2
     has been specified, the subroutine will not print a  title  and  the
     existing string in NAMEA will be used.
     The subroutine uses the CSI  to  parse  the  string  and  check  for







     DSLIB                                                       Page   4
                                                                30 Oct 80


     errors.  If an error is found, if a non-existent device is specified
     or if a carriage return is  typed,  the  routine  will  request  the
     filename  again.   This  will  also happen with MODE=2 if the string
     supplied in NAMEA is in error.
     If MODE=4 has not been specified, the subroutine will return at this
     point.
     If MODE=4 has been specified, and an input  file  is  required,  the
     subroutine  will  request  another  filename  if  the specified file
     cannot be found or has zero blocks.  If MODE=4  has  been  specified
     and  an  output  file  is required, a warning will be printed if the
     file already exists and the  routine  will  provide  the  option  of
     supplying another name.
     If a logical device name is specified,  the  corresponding  physical
     device name is printed by the subroutine.
     When the subroutine returns, IRET will indicate the number of blocks
     associated with the chosen filename.
     A non-file structured lookup to a directory device will be  rejected
     as will specification of a non existent device.


     ** NOTE **  When the subroutine returns, the chosen filename is  not
     associated with any logical unit or channel.  The call will normally
     be      followed      by      CALL ASSIGN(IUNIT,NAMEA,0,...)      or
     I=IASIGN(1,NAMER,NAMER(2),...).


     The following are two examples of typical calls  and  the  resulting
     dialog  with SPFILE with the routines responses UNDERLINED (assuming                                                     __________
     that RK1:  is assigned to DK:)

     INTEGER NAMER(4)
     BYTE NAMEA(15)
     DATA IEXT /3RDAT/
     CALL SPFILE(NAMER,NAMEA,IEXT,4,'TEST',IRET)

     at execution time:

     WHAT IS THE TEST FILE NAME ?  DDD:JIM <CR>     ____ __ ___ ____ ____ ____ _
     UNRECOGNIZED DEVICE DDD:     ____________ ______ ____
     WHAT IS THE TEST FILE NAME ?  JIM <CR>     ____ __ ___ ____ ____ ____ _
     FILE RK1:JIM.DAT NOT FOUND     ____ ___________ ___ _____
     WHAT IS THE TEST FILE NAME ?  TEST.LST <CR>     ____ __ ___ ____ ____ ____ _
     FILE RK1:TEST.LST FOUND     ____ ____________ _____

     At this point the subroutine returns with IRET equal to  the  number
     of blocks in the file RK1:TEST.LST.

     An example of the dialog for an output file with the call:
     CALL SPFIlE(NAMER,NAMEA,IEXT,5,'OUTPUT',IRET)

     WHAT IS THE OUTPUT FILE NAME ?  TEST.LST <CR>     ____ __ ___ ______ ____ ____ _
     FILE RK1:TEST.LST EXISTS - DO YOU WANT TO REPLACE IT ?  N     ____ ____________ ______ _ __ ___ ____ __ _______ __ _
     WHAT IS THE OUTPUT FILE NAME ?  JIM     ____ __ ___ ______ ____ ____ _
     OUTPUT FILE IS RK1:JIM.DAT     ______ ____ __ ___________








     DSLIB                                                       Page   5
                                                                30 Oct 80


     At this point the subroutine returns with IRET equal to -1.





























































     DSLIB                                                       Page   6
                                                                30 Oct 80


                            SUBROUTINE GETFIL                            __________ ______



     A routine to perform checks on a file specified as an ASCII  string.
     The  subroutine is primarily intended to be called by SPFILE but may
     be called directly if desired.


     The call is of the form:

          CALL GETFIL(NAMER,NAMEA,IEXT,IRET)

     where

          NAMER   Is a 4  word  integer  array  which  receives  a  RAD50
          representation of the filename.

          NAMEA   Is an array  which  is  assumed  to  contain  an  ASCII
          representation of the filename.

          IEXT    Is a 1-word RAD50 extension for the filename

          IRET    A parameter returned with the following significance:

                  IRET=-4  There was an error in the specification string
                  IRET=-3  The device name is unknown
                  IRET=-2  The file specified has zero blocks
                  IRET=-1  The file specified does not exist
                  IRET= 0  A non-file structured lookup was specified
                  IRET >0  An existing file of IRET blocks was found


     The subroutine calls the CSI in special mode to parse the string and
     uses  the  name  of  the  first input file returned.  The subroutine
     checks for a legal device  name  and  performs  a  lookup  with  the
     specified  filename.   A  non-file  structured lookup on a directory
     device is tested by calling IDSTAT.
























     DSLIB                                                       Page   7
                                                                30 Oct 80


                            SUBROUTINE FTRAN                            __________ _____



     A routine to generate an ASCII filename from a RAD50 specification


     The call is of the form:

          CALL FTRAN(NAMER,NAMEA)

     where

          NAMER   Is a 4 word integer array assumed to  contain  a  RAD50
          representation of the filename.

          NAMEA   Is a 15 byte array which receives  an  ASCII  character
          representation of the filename.


     The subroutine converts the four words in NAMER to an  ASCII  string
     and  inserts  a  colon  after  the  filename and a period before the
     extension unless the filename is blank.  The subroutine calls  TRIMS
     to  remove  any embedded spaces in the result.  The resultant string
     ends with a zero byte.





































     DSLIB                                                       Page   8
                                                                30 Oct 80


                            SUBROUTINE SPFILN                            __________ ______



     A routine to allow the specification of a filename numerically.


     The call is of the form:

          CALL SPFILN(NAMER,NAMEA,BASNAM,MODE,TITLE,IRET)

     where

          NAMER   Is a 4  word  integer  array  which  receives  a  RAD50
          representation of the filename.

          NAMEA   Is a 15 byte array which receives  a  13  or  14  ASCII
          character representation of the filename.

          BASNAM   Is a string of 14 ASCII characters which is  the  base
          filename from which the actual filename is formed.

          MODE    Is the mode of the call formed by adding  options  from
          the following list:

                  MODE =1  An output file is required (otherwise an input
                           file is assumed)
                  MODE =2  The existing string in NAMEA will be used  for
                           the filename
                  MODE =4  The routine will continue  to  request  a  new
                           filename   until  an  acceptable  response  is
                           typed.


          TITLE   Is a character string printed by  the  subroutine  when
          requesting the file number.

          IRET    Is a value returned by the subroutine as follows:

                  IRET=-5  A negative file number was specified
                  IRET=-4  Characters were typed but no file number
                  IRET=-3  A blank line was typed
                  IRET=-1  The specified file does not exist
                  IRET =0  A zero length file was found
                  IRET >0  An existing file of IRET blocks was found


     Unless MODE=2 has been included, the subroutine will request a  file
     number  by  printing  'WHAT  IS  THE <TITLE> NUMBER' and wait for an
     input line to be entered.  The input line will be  scanned  for  the
     existence  of  a  decimal  number.  If MODE=2 has been included, the
     existing string in NAMEA will be scanned for the file number.
     If only a <CR> is found in the line,  the  subroutine  returns  with
     IRET=-3.   If a line is found without a number, IRET=-4 is returned.
     If a negative number is found, IRET=-5 is returned.   These  returns                                                           _____  _______







     DSLIB                                                       Page   9
                                                                30 Oct 80


     occur regardless of the mode of the call.     _____ __________ __ ___ ____ __ ___ _____

     If a positive file number is found, the file number is then  encoded
     right  justified into the supplied base filename using I4 format and
     any resulting spaces are replaced  by  zeroes  to  form  the  actual
     filename.   For  example, if the base filename supplied in BASNAM is
     'RK0:DD0000.DAT' and the file number decoded is 23, then the  actual
     filename will be 'RK0:DD0023.DAT'.
     If MODE=4 has not been included,  the  subroutine  returns  at  this
     point.   If  MODE=4 has been included and an input file is required,
     the subroutine will request another file  number  if  the  specified
     file  cannot  be  found  or  has  zero  blocks.   If MODE=4 has been
     included and an output file is required, a warning will  be  printed
     if  the  file  already  exists  and  the option of supplying another
     number will be given.  For both input and output files  with  MODE=4
     included,  the  subroutine  will continue to request the file number
     until either an acceptable positive number is supplied  or  until  a
     response  is  given  which  causes  a return with IRET less than, or
     equal to -3.

     The basename must be a string of exactly 14 characters (ending  with
     a  zero  byte).  If a 2-character device name is required, the third
     character must be a blank e.g.  'DX :ZZ0000.DAT'.  If the letters in
     the  filename  are not required, or if a null extension is required,
     blanks may be used but the basename must be 14 characters.                                         ____





































     DSLIB                                                       Page  10
                                                                30 Oct 80


                            SUBROUTINE FREEFL                            __________ ______



     A routine to find the first non-existent file in a sequence of files
     specified numerically.

          CALL FREEFL(NAMER,NAMEA,BASNAM,ICHAN)

     where

          NAMER   Is a 4  word  integer  array  which  receives  a  RAD50
          representation of the filename.

          NAMEA   Is a 15 byte array which receives  a  13  or  14  ASCII
          character representation of the filename.

          BASNAM   Is a string of 14 ASCII characters which is  the  base
          filename from which the actual filename is formed.

          ICHAN    Is the channel to use for the lookup ( or -1 )

          The routine uses the same method as SPFILN  (q.v.)  to  form  a
          filename  starting with a file number of 1 and increasing by 10
          until a non-existent file is found.  Then 9 is subtracted  from
          the  file  number  and  the  routine  continues  to  search  in
          increments of 1 until a non-existent file is again found.
          If ICHAN is negative, a  channel  will  be  allocated  for  the
          lookup  otherwise  channel  ICHAN will be used.  In either case
          the channel will be free when the subroutine returns.
































     DSLIB                                                       Page  11
                                                                30 Oct 80


                            SUBROUTINE FCHECK                            __________ ______



     A routine to return information about a filename specified in ASCII.
     The  routine is primarily intended to be called by SPFILN and FREEFL
     but may be called directly if desired.


     The call is of the form:

          CALL FCHECK(NAMER,NAMEA,IRET,ICHAN)

     where

          NAMER   Is a 4  word  integer  array  which  receives  a  RAD50
          representation of the filename.

          NAMEA   Is a 15 byte array which must contain  a  14  character
          ASCII representation of the filename.

          IRET    Is a value returned by the subroutine as follows:

                  IRET=-2  A non-existent device was specified
                  IRET=-1  The specified file was not found
                  IRET =0  A zero length file was found  (or  a  non-file
                           structured lookup)
                  IRET >0  An input file was found (length=IRET)

          ICHAN   Is the channel to use ( or -1 )

     The subroutine converts the ASCII filename in NAMEA to  RAD50.   The
     filename  must  be  in the form DAT:ABCDEF.EXT or DK :ABCDEF.DAT.  A
     lookup on the file is then done using channel ICHAN.   If  ICHAN  is
     negative  a  channel  will  be  allocated  for  the lookup otherwise
     channel ICHAN will be used.  In either case the channel will be free
     when the subroutine returns.

























     DSLIB                                                       Page  12
                                                                30 Oct 80


                         INTEGER FUNCTION YESCHK                         _______ ________ ______



     A routine to give a numerical value in response to a question  which
     asks for a 'YES' or 'NO' reply.


     The call is of the form:

          I=YESCHK(0)   or   IF(YESCHK(0).EQ.0)IFLAG=1

     When called, the function waits for a string to be  entered  on  the
     console  device.   If  the  response begins with the letter <Y>, the
     value of the function is 0.  If the response is a simple  <CR>,  the
     value of the function is -1.  Any other response returns a value for
     the function of 1.

     The function should be declared INTEGER in the calling program.











































     DSLIB                                                       Page  13
                                                                30 Oct 80


                            SUBROUTINE GETSTC                            __________ ______



     A routine to fetch an  input  line  from  the  console  or  from  an
     indirect  file.  The subroutine is used by SPFILE, SPFILN and YESCHK
     but may be called directly if desired.


     The call is of the form:

          CALL GETSTC(STRING,ILEN)

     where

          STRING  Is the string to receive input.

          ILEN  is the maximum length for the string.



     The subroutine uses GETLIN to fetch an input line into  an  internal
     81  byte  buffer.  The string is then copied up to a maximum of ILEN
     bytes into STRING by a call to SCOPY.






































     DSLIB                                                       Page  14
                                                                30 Oct 80


                            SUBROUTINE TRIMS                            __________ _____



     A routine to remove embedded spaces from a string.


     The call is of the form:

          CALL TRIMS(LINE)

     where

          LINE  Is the line to be packed



     All spaces are removed from the line which may  be  any  length  but
     must end in a zero byte.











































     DSLIB                                                       Page  15
                                                                30 Oct 80


                             SUBROUTINE LNUM                             __________ ____



     A routine to extract real numbers in free format from a string


     The call is of the form:

          CALL LNUM(LINE,ARAY,NUM)

     where

          LINE  Is a string from which numbers are extracted.

          ARAY  Is a real array which receives the extracted numbers.

          NUM   Is the maximum number of numbers to be extracted.


     The string LINE is searched for the occurrence of  decimal  numbers.
     The  string may be of any length but must end with a zero byte.  Any
     non-numeric character, except period,  terminates  a  number  and  a
     minus  sign  preceding  a number negates it.  If less than N numbers
     are found in the line, the parameter N  is  set  to  the  number  of
     numbers actually found.  Thus the parameter N must be a variable.




































     DSLIB                                                       Page  16
                                                                30 Oct 80


                            SUBROUTINE ILNUM                            __________ _____



     A routine to extract integers in free format from a string


     The call is of the form:

          CALL ILNUM(LINE,IRAY,NUM)

     where

          LINE  Is a string from which numbers are extracted.

          IRAY  Is an integer array which receives the extracted numbers.

          NUM   Is the maximum number of numbers to be extracted.


     The string LINE is searched for the occurrence of  decimal  numbers.
     The  string may be of any length but must end with a zero byte.  Any
     non-numeric character terminates a number and a minus sign preceding
     a  number negates it.  If less than N numbers are found in the line,
     the parameter N is set to the  number  of  numbers  actually  found.
     Thus the parameter N must be a variable.  If a number whose absolute
     value is greater than 32767 is found,  a  value  of  32767  with  an
     appropriate sign is returned.


































     DSLIB                                                       Page  17
                                                                30 Oct 80


                            SUBROUTINE RENAME                            __________ ______



     A subroutine to facilitate the renaming of files.


     The call is of the form:

          CALL RENAME(ICHAN,OLDNAM,NEWNAM)

     where

          ICHAN   Is the channel number to use for the rename ( or -1 )
          OLDNAM  Is the old filename
          NEWNAM  Is the new filename


     The subroutine copies the filenames into an 8 word block  and  calls
     IRENAM  for  the  rename.   Channel  ICHAN  is  used unless ICHAN is
     negative, in which case a  channel  is  requested  and  subsequently
     freed.   If  the  file being renamed is generated within the calling
     program, it must be closed before it can be renamed.







































     DSLIB                                                       Page  18
                                                                30 Oct 80


                            SUBROUTINE RFILT                            __________ _____



     A routine to perform triangular or trapezoidal filtering of  a  real
     array


     The call is of the form:

          CALL RFILT(A,B,M,N)

     where

          A  Is the input array, type REAL, dimension M
          B  Is the output array, type REAL, dimension M
          M  Is the length of the array to be filtered
          N  Is the type of filtering as follows:

               N=0  No filtering - a copy is performed.
               N=1  A running triangular window is used.
               N=2  A running trapezoidal window is used.


     **NOTE** A and B may be the same array


     The subroutine uses time domain convolution of the  input  array  to
     generate  the  output  array.  If triangular filtering is specified,
     the function is:

          B(I)=.25*A(I-1)+.5*A(I)+.25*A(I+1)

     If trapezoidal filtering is specified, the function is:

          B(I)=.125*A(I-2)+.25*A(I-1)+.25*A(I)+.25*A(I+1)+.125*A(I+2)

     At the ends of the array, the data is treated as if  the  first  and
     last samples were repeated.























     DSLIB                                                       Page  19
                                                                30 Oct 80


                            SUBROUTINE VALDAT                            __________ ______



     A routine to ensure that the date has been entered.


     The call is of the form:

          CALL VALDAT

     The subroutine calls IDATE to verify that a date has been specified.

     If a date has not been entered the calling program will  be  aborted
     with the message 'PLEASE ENTER THE DATE'















































     DSLIB                                                       Page  20
                                                                30 Oct 80


                            SUBROUTINE ASLOOK                            __________ ______



     A MACRO subroutine to find the physical device name associated  with
     a logical device name in the assignment tables


     The call is of the form:

          CALL ASLOOK(INAME,JNAME,IVERSN)

     where

          INAME   Is a RAD50 logical device name
          JNAME   Receives the corresponding physical device name
          IVERSN  Is the RT-11 version number

          **NOTE** INAME and JNAME may be the same variable

          The RT-11 version number is extracted from the monitor base and
          stored  in  IVERSN.   Under Version 2, the location of the UNAM
          tables is known and  the  subroutine  proceeds  to  lookup  the
          assignment.   If  the monitor is version 3 or 4, the assignment
          table is found  by  searching  the  resident  monitor  for  the
          permanent  assignments  of  SY:   and DK:.  Once the assignment
          tables are found, the physical assignment for INAME  is  sought
          and stored in JNAME.  If no assignment is found, JNAME is equal
          to INAME unless INAME is DK:  in which case, JNAME  is  set  to
          SY:.
          If the version number is greater than 4,  the  subroutine  does
          not  try  to  find the tables ( although it might be able to ),
          but merely sets JNAME equal to INAME.