A Library Implementation
                                   of
                          Programmed Requests
                                  for
                              TSX/TSX-Plus








                          N. A. Bourgeois, Jr.
                      Sandia National Laboratories
                   Systems Engineering Division 1738
                             P. O. Box 5800
                         Albuquerque, NM 87185








                                Abstract


             A library  of  FORTRAN  callable  subroutines  that
        implement  EMT's  provided by TSX/TSX-Plus is described.
        Calling  sequences,  library  building  procedures   and
        source codes are given.








                                 80j13b


                                                        Page   1
                                                       16 Oct 80


















                This  document  is  issued   by   Sandia
                National  Laboratories, operated for the
                United States Department  of  Energy  by
                Sandia Corporation.


                                 Notice


                This  document  was  sponsored  by   the
                United  States  Government.  Neither the
                United States Government nor the  United
                States  Department of Energy, nor any of
                their  employees,  nor  any   of   their
                contractors,  subcontractors,  or  their
                employees makes any warranty, express or
                implied,  or assumes any legal liability
                or  responsibility  for  the   accuracy,
                completeness   or   usefulness   of  any
                information,   apparatus,   product   or
                process  disclosed,  or  represents that
                its use  would  not  infringe  privately
                owned rights.


                This work was sponsored and funded by:

                    Headquarters, ESD / OCB / Stop 36
                    Hanscom Air Force Base, MA 01731


                                                        Page   2
                                                       16 Oct 80






                              Introduction


             When application programs are executed under a time
        sharing  executive,  such  as  TSX  or  TSX-Plus  [1,2],
        certain capabilities become desirable if  not  absolutly
        essential.   These  capabilities  relate to requirements
        for such things as hardware dependent I/O, shared  files
        and  inter-program communication.  Both TSX and TSX-Plus
        provide a number of programmed  requests  or  EMT's  for
        this purpose.

             This paper describes a number of  FORTRAN  callable
        subroutines  and  their calling sequences that implement
        these  EMT's.   All  of  the  routines  are  written  in
        MACRO-11 [3].  They provide facilities that permit files
        to be shared, that allow running programs to communicate
        with  each other, that determine the TSX line number and
        that determine the amount of free space available in the
        spool  file.  Procedures for building a library of these
        routines are also presented [4].  Source code  is  given
        in the appendix.



                       Communication Subroutines
                               MSGCOM.MAC


             Three subroutines provide the facilities that allow
        running  programs to communicate with each other.  These
        message communication facilities allow programs to  send
        messages  through  named  channels,  check to see if any
        messages are pending and to suspend  execution  until  a
        message  is received.  Suitable error codes are returned
        as required.  The calling sequence is as follows:

                CALL XXXXXX (CHNAME,MSGBUF,MSGSIZ,IERR)

        Where:  XXXXXX  Subroutine name as follows:

                        SNDMSG  Send a message.

                        RCVMSG  Receive  a  message,  return  if
                                none pending.

                        RCVMSW  Receive a message, wait for  one
                                if none pending.


                                                        Page   3
                                                       16 Oct 80


                CHNAME  Six ASCII character name of the  message
                        channel.    Must   be   six  characters,
                        backfill with spaces if necessary.

                MSGBUF  Name of the string array containing  the
                        message.

                MSGSIZ  Message length in characters.

                IERR    Error code returned as follows:

                        0       No error.

                        1       All message channels busy.

                        2       Maximum   allowed   number    of
                                messages.

                        3       No message  is  pending  on  the
                                named channel.

                        4       Message was  too  long  and  was
                                truncated to maximum length.



                              Shared Files
                               RCDLOK.MAC


             Four subroutines provide record locking  facilities
        that  are  useful in situations where programs being run
        from several terminals wish to  update  a  common  file.
        Through  these  record  locking facilities a program may
        gain exclusive access to one or more blocks in  a  file.
        Other programs attempting to lock the same block(s) will
        be denied access until the first  program  releases  the
        locked  block(s).   Suitable error codes are returned as
        required.  The calling sequence is as follows:

                     CALL XXXXXX (ICHN[,IBLK],IERR)

        Where:  XXXXXX  Subroutine name as follows:

                        SHRFIL  Declare a shared file.

                        LKBLK   Lock a block, return if  already
                                locked.

                        LKBLKW  Lock a block,  wait  if  already
                                locked.

                        UNLBLK  Unlock all locked blocks.

                ICHN    Channel number open to the file.


                                                        Page   4
                                                       16 Oct 80


                IBLK    Number  of  the  block  to  be   locked.
                        Required for LKBLK and LKBLKW only.

                IERR    Error code returned as follows:

                        0       No error.

                        1       Channel not open to a file.

                        2       Too  many  channels  opened   to
                                shared files.

                        3       Too many shared files opened.

                        4       Channel not  open  to  a  shared
                                file.

                        5       Request to lock too many blocks.

                        6       Requested  block  is  locked  by
                                another user.



                       Miscellaneous Subroutines
                               TSXMSC.MAC


             The first of these subroutines is used to determine
        if  TSX  is  running  and if so the TSX line number.  It
        returns a single positive integer value to  the  calling
        program.   If  TSX  is not running the value returned is
        zero.  If TSX is running the value returned is  the  TSX
        line  number.   The  second  subroutine  determines  the
        integer value of the number of free blocks available  in
        the  spool  file.   Neither  routine  returns  any error
        codes.  The calling sequence is as follows:

                           CALL XXXXXX (IVAL)

        Where:  XXXXXX  Subroutine name as follows:

                        TSXTST  Determine the TSX line number.

                        SPLBLK  Determine  the  number  of  free
                                blocks.

                IVAL    The integer value returned.


                                                        Page   5
                                                       16 Oct 80


                            Library Building
                               TSXLIB.COM


             The following outlines the procedures to build  and
        use  the several subroutines in a library format.  RT-11
        command strings to assemble the routines and build  them
        into  a  library  are  given.   Also  shown  are command
        strings to compile an application program  and  link  it
        with the library.

                .RUN MACRO
                *MSGCOM[,LP:/C]<MSGCOM
                *RCDLOK[,LP:/C]<RCDLOK
                *TSXMSC[,LP:/C]<TSXMSC
                *^C

                .RUN LIBR
                *TSXLIB<MSGCOM,RCDLOK,TSXMSC
                *^C

                .RUN FORTRAN
                *PRGRM[,LP:]<PRGRM/W
                *^C

                .RUN LINK
                *PRGRM[,LP:/A/W]<PRGRM,TSXLIB/F
                *^C


                                                        Page   6
                                                       16 Oct 80






                               References


        1.  "TSX Timesharing Reference Manual",  S & H  Computer
            Systems, Inc., Nashville, TN, August 1978.

        2.  "General Release Notes for TSX-Plus",  Version  1.4,
            S & H Computer Systems, Inc., Nashville, TN.

        3.  "PDP-11   MACRO-11   Language   Reference   Manual",
            AA-5075B-TC, Digital Equipment Corporation, Maynard,
            MA, January 1980.

        4.  "RT-11 System User's  Guide",  AA-5279B-TC,  Digital
            Equipment Corporation, Maynard, MA, March 1980.




































                                                        Page   7
                                                       16 Oct 80






                                Appendix


             The following pages contain source listings of  the
        code   implementing   the   various  subroutines.   Also
        included is a listing of an  indirect  command  file  to
        build the library.













































                                                        Page   8
                                                       16 Oct 80


        .TITLE  MSGCOM.MAC

                .IDENT  \80H08A\        ;VERSION
                .PSECT  USER$I,I        ;CODE
                .PSECT  USER$D,D        ;DATA

                ERRBYT  =53             ;ERROR CODE LOCATION

        MSGCOM::
        EMTBLK: .BYTE   0               ;EMT CODE
                .BYTE   0
                .WORD   0               ;SA CHANNEL NAME
                .WORD   0               ;SA MESSAGE BUFFER
                .WORD   0               ;ADDR MESSAGE SIZE

                .PSECT  USER$I

        ;SEND A MESSAGE IN A NAMED CHANNEL.
        SNDMSG::MOV     #104,R1         ;EMT CODE
                JSR     PC,DOIT         ;SEND THE MESSAGE
                RTS     PC

        ;RECEIVE A PENDING MESSAGE ON A NAMED CHANNEL.  RETURN
        ;WITH AN ERROR CODE IF NONE IS PENDING.
        RCVMSG::MOV     #105,R1         ;EMT CODE
                JSR     PC,DOIT         ;RECEIVE THE MESSAGE
                RTS     PC

        ;RECEIVE A MESSAGE ON A NAMED CHANNEL.  WAIT FOR ONE IF
        ;NONE IS PENDING.
        RCVMSW::MOV     #106,R1         ;EMT CODE
                JSR     PC,DOIT         ;RECIEVE THE MESSAGE
                RTS     PC

        DOIT:   MOV     #EMTBLK,R0      ;POINT TO EMT AREA
                CLRB    (R0)+           ;BUMP THE POINTER
                MOVB    R1,(R0)+        ;EMT CODE
                MOV     @2(R5),(R0)+    ;SA CHANNEL NAME
                MOV     @4(R5),(R0)+    ;SA MESSAGE BUFFER
                MOV     @6(R5),(R0)     ;ADDR MESSAGE SIZE
                CLR     @10(R5)         ;ERROR CODE
                EMT     375             ;NOW LET TSX DO IT
                BCC     1$              ; IF NO ERROR
                MOVB    @#ERRBYT,@10(R5) ; IF ERROR
        1$:     RTS     PC

                .END


                                                        Page   9
                                                       16 Oct 80


        .TITLE  RCDLOK.MAC

                .IDENT  \80H08A\        ;VERSION
                .PSECT  USER$I,I        ;CODE
                .PSECT  USER$D,D        ;DATA

                ERRBYT  =53             ;ERROR CODE LOCATION

        RCDLOK::
        EMTBLK: .BYTE   0               ;EMT CODE
                .BYTE   0               ;CHANNEL NUMBER
                .WORD   0               ;BLOCK NUMBER

                .PSECT  USER$I

        ;TELL TSX THAT A FILE IS TO BE SHARED AND THAT RECORD
        ;LOCKING WILL BE PERFORMED.
        SHRFIL::MOV     #100,R1         ;EMT CODE
                CLR     R2              ;ERROR CODE OFFSET
                JSR     PC,DOIT2        ;TELL TSX SHARED FILE.
                RTS     PC

        ;UNLOCK ALL BLOCKS THAT WERE PREVIOUSLY LOCKED ON THE
        ;SHARED FILE.
        UNLBLK::MOV     #101,R1         ;EMT CODE
                MOV     #3,R2           ;ERROR CODE OFFSET
                JSR     PC,DOIT2        ;UNLOCK ALL BLOCKS
                RTS     PC

        DOIT2:  MOV     #EMTBLK,R0      ;POINT TO EMT AREA
                MOVB    @2(R5),(R0)+    ;CHANNEL NUMBER
                MOVB    R1,(R0)         ;EMT CODE
                CLR     @4(R5)          ;ERROR CODE
                EMT     375             ;HAVE TSX DO IT
                BCC     1$              ; IF NO ERROR
                ADD     R3,@#ERRBYT     ; IF
                MOVB    @#ERRBYT,@4(R5) ;  ERROR
        1$:     RTS     PC

        ;LOCK A SPECIFIC BLOCK OF A SHARED FILE.  WAIT IF THE
        ;BLOCK IS ALREADY LOCKED BY ANOTHER USER.
        LKBLKW::MOV     #102,R1         ;EMT CODE
                JSR     PC,DOIT3        ;LOCK A BLOCK AND WAIT
                RTS     PC

        ;LOCK A SPECIFIC BLOCK OF A SHARED FILE.  RETURN WITH AN
        ;ERROR CODE IF THE BLOCK IS ALREADY LOCKED BY ANOTHER
        ;USER.
        LKBLK:: MOV     #103,R1         ;EMT CODE
                JSR     PC,DOIT3        ;LOCK A BLOCK AND RETURN
                RTS     PC

        DOIT3:  MOV     #EMTBLK,R0      ;POINT TO EMT AREA
                MOVB    @2(R5),(R0)+    ;CHANNEL NUMBER
                MOVB    R1,(R0)+        ;EMT CODE


                                                        Page  10
                                                       16 Oct 80


                MOV     @4(R5),(R0)     ;BLOCK NUMBER
                CLR     @6(R5)          ;ERROR CODE
                EMT     375             ;LOCK THE BLOCK
                BCC     1$              ; IF NO ERROR
                ADD     #3,@#ERRBYT     ; IF
                MOVB    @#ERRBYT,@6(R5) ;  ERROR
        1$:     RTS     PC

                .END




        .TITLE  TSXTST.MAC

                .IDENT  \80H10A\        ;VERSION
                .PSECT  USER$I,I        ;CODE
                .PSECT  USER$D,D        ;DATA

        TSXMSC::
        EMTBLK: .BYTE   0               ;EMT CODE
                .BYTE   0

                .MCALL  .HERR           ;LET MONITOR INTERCEPT
                                        ; FATAL ERRORS
                .MCALL  .SERR           ;INTERCEPT FATAL ERRORS

                .PSECT  USER$I

        ;DETERMINE THE TSX LINE NUMBER.
        TSXTST::.SERR                   ;INTERCEPT FATAL ERRORS
                MOV     #107,R1         ;EMT CODE
                JSR     PC,DOIT         ;GET THE LINE NUMBER
                .HERR                   ;LET MONITOR INTERCEPT
                RTS     PC              ; FATAL ERRORS

        ;DETERMINE THE NUMBER OF FREE BLOCKS IN THE SPOOL FILE.
        SPLBLK::MOV     #110,R1         ;EMT CODE
                JSR     PC,DOIT         ;GET NUMBER OF BLOCKS
                RTS     PC

        DOIT:   MOV     #EMTBLK,R0      ;SET THE POINTER
                CLRB    (R0)+           ;BUMP THE POINTER
                MOVB    R1,(R0)         ;EMT CODE
                EMT     375             ;GET THE INTEGER VALUE
                BCS     1$              ; IF ERROR
                MOV     R0,@2(R5)       ; RETURN INTEGER VALUE
                BR      2$
        1$:     CLR     @2(R5)          ;RETURN ZERO VALUE
        2$:     RTS     PC

                .END


                                                        Page  11
                                                       16 Oct 80


        ! TSXLIB.COM
        ASS     RK0:    SYS:    ! BOOTED SYSTEM.
        ASS     RK2:    SRC:    ! SOURCE MEDIA.
        ASS     RK3:    TMP:    ! SCRATCH MEDIA.
        ASS     RK3:    LST:    ! LISTING DEVICE.
        RUN     MACRO
        TMP:MSGCOM,LST:MSGCOM<SRC:MSGCOM
        TMP:RCDLOK,LST:RCDLOK<SRC:RCDLOK
        TMP:TSXMSC,LST:TSXMSC<SRC:TSXMSC
        ^C
        RUN     LIBR
        TMP:TSXLIB,LST:TSXLIB/W<TMP:MSGCOM,RCDLOK,TSXMSC
        ^C
        SET     ERROR   NONE
        REN/NOP SYS:TSXLIB.OBJ  SYS:
        SET     ERROR   ERROR
        COP/PRE TMP:TSXLIB.OBJ  SYS:
        REN/PRO SYS:TSXLIB.OBJ  SYS:
        COP     SRC:TSXLIB.COM  LST:
        ! END OF FILE.