MXV22

                                     DISK CONTROLLER

 
                                         MANUAL

























































                                            
















                                         PREFACE

         The purpose of this manual is to provide the user adequate information
         to configure and operate the MXV22 floppy disk controller.  The
         information provided should clarify the controller connection to any
         Shugart compatible drive and assist in the selection of associated
         interface options.  Both register definition and command protocol are
         provided for reference and as an aid in development of user software. 
         Operational procedures outline the use of the controller features as
         well as explaining operation in an RT-11 or RSX11M software
         environment.




































                                            













                                                                SECTION 1


                                                                GENERAL
                                                                INFORMATION


      1. INTRODUCTION         ____________

         The MXV22 is a dual density controller compatible with the DEC* RX02
         floppy disk system.  The MXV22 emulates two separate RXV21 controllers,
         each of which controls two 8-inch floppy disk drives.  When configured
         with any Shugart compatible drive, it is a direct replacement for two
         complete RX02 subsystems.  The controller provides either single
         density encoding compatible with IBM 3740 equipment or double density
         encoding providing up to 1 Mbyte of storage on a single diskette.

         All electronics are contained on one dual-height board which plugs
         directly into any standard LSI-11 backplane and interfaces through a 50
         conductor ribbon cable with up to four (4) Shugart compatible drives. 
         All controllers are 100% tested and ready for operation.  The primary
         controller registers are configured for the standard device address
         177170U8D and interrupt vector 264U8D.  The secondary controller registers
         are configured with a device address of 177174U8D and interrupt level is
         factory set to level four.  Features include:

         .22 bit addressing

         .Transparent firmware bootstrap automatically loads either single
          or double density diskettes.

         .Formatting capabilities permit writing sector headers, checking
          the written headers, and writing the data fields in the user
          selected density.

         .Jumper selection of both alternate address and vector.

         .Jumper selectable four-level device interrupt priority compatible
          with the LSI-11/23.

         .Provides power fail protection for data integrity.

         .Write current control signal for tracks greater than forty-three.

         .Write precompensation for reduced error rates.

         *DEC, PDP-11 LSI-11, RSX, Unibus & Q bus are registered trademarks of
         Digital Equipment Corporation.


                                            1







    1.1. COMPONENTS         __________

         The controller is provided with the following components:

                        P/N 81010-07-2   Floppy disk controller
                        M 81010-02-2     MXV22 disk controller manual



    1.2. COMPATIBILITY         _____________

         This section discusses the aspects of hardware, software and media
         compatibility with Digital Equipment's RX02 system.  The information
         will aid the user in data interchanging with foreign systems.

 
                                        Hardware 
                                        ________

         The controller is compatible with the LSI-11, LSI-11/2 and LSI-11/23
         processors. All circuitry is contained on one dual-wide board that
         plugs directly into any standard LSI-11 backplane.  Alternate address
         selection and a four-level device interrupt priority scheme provide the
         user added flexibility for expanded system configurations.  Shugart
         compatible drive logic is interfaced through a 50-pin ribbon cable. 
         The connector pins are compatible with both the 800 and 850 series
         drives.

 
                                        Software 
                                        ________

         The MXV22 is completely compatible with RXV21 register definition and
         command protocol.  All DEC-supplied software designed to operate with
         the RX02 system will operate with the controller without modification.

                                          Media                                          _____

         The media used with the MXV22 are  compatible with the IBM 3740 family
         of equipment.  Either preformatted or blank soft sectored diskettes may
         be used with the controller.  The following list summarizes the
         suggested media.

                        IBM                Single or Double Density
                        DEC                RX01/RX02















                                            2







  1.2.1. Logical Track Format         ____________________

         The diskette surface is divided into 77 concentric tracks numbered
         0-76.  Each track consists of 26 sectors numbered 1-26.  The track
         begins and ends at the index address mark.  The track is formatted in
         such a way that this "soft" index is preceded by the leading edge of
         the physical index hole in the diskette.  Following the physical index
         are 40 bytes of "FF" data, 6 bytes of "0" data, and the index address
         mark indicating the beginning of the track.  Following the index
         address mark is the post index gap consisting of 26 bytes of "FF" data
         and 6 bytes of "0" data.  The next field is the sector header for
         sector 1.  Following the data field is the data gap consisting of 28
         bytes of "FF" data and 6 bytes of "0" data.  This field leads to the
         next sector header.  Following the 26th data record is the pre-index
         gap consisting of approximately 274 bytes of "FF" data.

         Each track is formatted in the above manner.  Refer to Figure 1-1.  The
         sector header field of each sector contains information describing the
         sector number, track number, and diskette side.  All the above fields
         are recorded in FM except as noted in the following sections.






























                            Figure 1-1:  Logical Track Format





                                            3







  1.2.2. Sector Header Field         ___________________

         The header field consists of 7 bytes of information.  Preceding the
         header is a field of 6 bytes of "zero" data for synchronization.  The
         header and this preamble are always recorded in FM.


                   1.   Byte 1.  ID Address Mark - A unique mark
                        consisting of 1 byte of FE (hex) data with
                        three missing clock-transitions using a C7
                        (hex) clock pattern.  This mark is decoded by
                        the controller and indicates the start of the
                        sector header.

                   2.   Byte 2.  Track Address - This byte indicates
                        the absolute (0-114U8D) track address.  Each
                        sector contains this track information to
                        locate its position on one of the 77 tracks.

                   3.   Byte 3.  Side - This byte indicates the
                        diskette side (0 or 1).

                   4.   Byte 4.  Sector Address - This byte indicates
                        the absolute (1-32U8D) sector address.  Each
                        sector contains this information to identify
                        its position on the track.

                   5.   Byte 5.  "Zero"

                   6.   Byte 6, 7.  CRC - This is the 16 bit cyclic
                        redundancy character and is calculated for
                        each header from the first 5 bytes of
                        information, using the IBM 3740 polynomial. 
                        (Refer to Cyclic Redundancy Check, Section
                        1.2.7.).



  1.2.3. Data Field         __________

         The data field consists of either 131U10D or 259U10D bytes of information
         depending upon the recording method.  Preceding the data field is a
         field of 6 bytes of "zero" data for synchronization.

         The preamble and data address mark are always written in FM.  The user
         data and CRC character are either written in FM or MFM modified
         depending upon the formatted diskette density.









                                            4







         1.   Byte 1.  Data Address Mark - A unique mark consisting of a
              data byte (see Table 1-1) with three missing clock
              transitions using a C7 (hex) clock pattern.  This byte is
              always written in FM and is decoded by the controller to
              indicate the start of the data field, its recording method
              (FM vs MFM), and if the field is a deleted data field.

               ------------------------------------------------
              |  ADDRESS    |  INDICATED  |  DATA   |  CLOCK   |
              |   MARK      |   DENSITY   |         |          |
              |------------------------------------------------|
              |------------------------------------------------|
              |  INDEX      |      NA     |   FC    |    D7    |
              |------------------------------------------------|
              |    ID       |      NA     |   FE    |    C7    |
              |------------------------------------------------|
              |             |      FM     |   FB    |    C7    |
              |   DATA      |----------------------------------|
              |             |   Modified  |   FD    |    C7    |
              |------------------------------------------------|
              |  DELETED    |      FM     |   F8    |    C7    |
              |   DATA      |----------------------------------|
              |             |   Modified  |   F9    |    C7    |
               ------------------------------------------------

                           Table 1-1:  Address Marks

         2.   Bytes 2-129 (FM) or Bytes 2-257 (MFM Modified).  User Data. 
              This field is recorded in either FM or MFM modified. 
              Depending upon the encoding scheme, either 128 or 256 bytes
              of information can be stored.

         3.   Bytes 130-131 or 258-259.  CRC - This is the 16 bit cyclic
              redundancy character and is calculated for each data field
              from the first 129 or 257 bytes of information using the IBM
              3740 polynomial.  (Refer to Cyclic Redundancy Check, Section
              1.2.7.).  These bytes are recorded with the same encoding
              scheme as the data field.



  1.2.4. Recording Scheme         ________________

         Two recording schemes are used by the MXV22:  double frequency (FM) and
         DEC modified Miller code (MFM).  FM is used for single density
         recording and is compatible with IBM 3740 or DEC RX01 media.  DEC
         modified MFM is used for recording double density and is only
         compatible with the DEC RX02 system.








                                            5







  1.2.5. Double Frequency (FM)         _____________________

         FM recording is characterized by a flux transition at the beginning of
         each bit cell which is commonly termed a clock pulse or transition as
         shown in Figure 1-2.  A logic "one" is represented by a flux transition
         withing the bit cell; a logic "zero" is represented by the lack of any
         flux transition within a bit cell.  In FM the bit cell time is 4us.

                "0"       "0"       "1"       "0"       "1"       "0"
            _         _         _    _    _         _    _    _         _
           | |       | |       | |  | |  | |       | |  | |  | |       | |
         --   -------   -------   --   --   -------   --   --   -------   --
            C         C         C    D    C         C    D    C         C
            |   bit   |
         -->|   cell  |<--
            |   4us   |

                        Figure 1-2:  FM Recording Characteristics


  1.2.6. DEC Modified MFM         ________________

         MFM recording consists of flux transitions for a logic "one" and no
         flux transitions for a logic "zero".  A clock transition only occurs
         between two consecutive logic "zeros" as shown in Figure 1-3 below. 
         The MFM bit cell time is 2us.


            "1"   "1"  "0"     "0"  "1"   "0"   "1"   "1"
             _     _        _        _           _     _
            | |   | |      | |      | |         | |   | |
         ---   ---   ------   ------   ---------   ---   ---
             D     D        C        D           D     D
             | bit |
          -->| cell|<--
             | 2us |

 
                       Figure 1-3:  MFM Recording Characteristics


















                                            6






         Table 1-2 summarizes the standard MFM encoding algorithm.

              ------------------------------------------------
              |        DATA       |         ENCODED DATA       |
              |------------------------------------------------|
              |  DN-1        DN   |    DN-1     CN      DN     |
              |------------------------------------------------|
              |    0         0    |     0        1       0     |
              |    1         0    |     1        0       0     |
              |    0         1    |     0        0       1     |
              |    1         1    |     1        0       1     |
               ------------------------------------------------

                    Table 1-2:  Standard MFM Encoding

              Because single density headers are used for both FM and MFM
              recording formats, and since certain MFM patterns map into single
              density address marks, a modified algorithm is used.  The mapping
              occurs when a data pattern of exactly four consecutive "ones" is
              encoded.  Whenever this pattern is encoded a special algorithm is
              applied.  Table 1-3 defines the encoding algorithm for this
              special case.

               -----------------------------------------------------------
              |                           DATA                            |
              |-----------------------------------------------------------|
              |  DN-5   | DN-4    |  DN-3   |  DN-2   |  DN-1   |   DN    |
              |-----------------------------------------------------------|
              |    0    |   1     |    1    |    1    |    1    |   0     |
              |-----------------------------------------------------------|
              |  X   0  | 1   0   |  0   0  |  1   0  |  0   0  |  1  0   |
              |CN-5 DN-5|CN-4 DN-4|CN-3 DN-3|CN-2 DN-2|CN-1 DN-1| CN  DN  |
              |-----------------------------------------------------------|
              |                       ENCODED DATA                        |
               -----------------------------------------------------------
                         
                       Table 1-3:  Modifying Algorithm (Special Case)

              When reading double density data fields the controller checks for
              a missing clock bit between two zero data cells, and if found,
              substitutes ones for the two zero data bits (generated by the
              special encoding algorithm).


  1.2.7. Cyclic Redundancy Check         _______________________
         Each sector header field and data field has two byte CRC character
         appended.  This 16 bit character is the remainder that results when
         dividing the data bits [represented as a polynomial M(x)] by a
         generator polynomial G (x).  The polynomial used for IBM 3740 is G(x) =
         X D16U+ X D12U+ X D5U+ 1.  For the sector header the data bits include byte 1
         thru 5.  For an FM data field the data bits include byte 1 thru byte
         129.  For an MFM data field the data bits include byte 1 thru byte 257.





                                            7







    1.3. SPECIFICATIONS         ______________

         RECORDING TECHNIQUE:

           Single Density       IBM 3740 FM
           Double Density       DEC Modified MFM

         POWER REQUIREMENTS:

           Voltage              Single 5V supply
                                (from LSI-11 backplane)
           Current              2.5A typical

         ENVIRONMENTAL

           Temperature          0 degree - 45 degrees C
           Humidity             10% - 95% non-condensing







































                                            8














                                                                  SECTION 2


                                                                  INSTALLATION



      2. GENERAL         _______

         The controller is shipped with standard options configured.  The
         standard address 177170U8D and vector 264U8D are set.  The device interrupt
         priority is set to level four.  The firmware bootstrap is disabled.

         Most options are factory foil-etched to the most often used
         configuration.  The foil jumpers must first be cut before the alternate
         jumpers are inserted.  Refer to Tables 2-1, 2-2, and 2-3 for alternate
         options and Figure 2-1 for jumper location.  Several of the options are
         selectable by using AMP 530153-2 pin jumpers.  If these pin jumpers are
         not available use #30 wire wrap.


    2.1. CONFIGURATION         _____________



  2.1.1. Address Vector Selection         ________________________

         The controller is shipped with the DEC standard device address and
         vector assignments preset to 177170U8D and 264U8D, respectively.  Any
         change in these assignments would necessitate a change in system
         software.  However, a dual address and vector option is selectable
         enabling a second register assignment at 177174U8D and 270U8D,
         respectively.

         The dual address mode is used in applications requiring more than two
         drives.  In this case the controller simulates the operation of two
         controller as required by standard DEC software.  To select this option
         remove the jumper between W16 and W17.  Jumper W15 to W16 and jumper W7
         to W8 as shown in Table 2-1.










                                            9







                    --------------------------------------------------
                   |                   |           JUMPERS            |
                   |   OPTION          |------------------------------|
                   |                   |  15-16  |  16-17  |   7-8    |
                   |--------------------------------------------------|
                   |  Standard         |         |         |          |
                   |  Address/Vector*  |   OUT   |    IN   |   OUT    |
                   |  177170/264       |         |         |          |
                   |--------------------------------------------------|
                   |  Dual             |         |         |          |
                   |  Address/Vector   |    IN   |   OUT   |    IN    |
                   |  177170/264       |         |         |          |
                   |  177174/270       |         |         |          |
                   |--------------------------------------------------|
                   |  *Factory Preset                                 |
                    --------------------------------------------------

                       Table 2-1:  Address/Vector Option Configuration

  2.1.2. Device Interrupt Priority         _________________________

         The MXV22 supports the four-level device interrupt priority scheme
         compatible with the LSI-11/23.  The controller asserts interrupt
         requests and monitors higher level request lines during interrupt
         arbitration as described in Table 2-2.  The level four request is
         always asserted by the controller, regardless of its priority, to
         maintain compatibility with the LSI-11 and LSI-11/2 processors.
         The interrupt priority level is configured to level four at the
         factory.  If a different interrupt level is desired the following
         foil-etched jumpers must be cut.  Refer to Table 2-2 for the proper
         jumpers to insert for the desired priority level.

                        W19 - W20          W28 - W29
                        W22 - W23          W30 - W31
                        W24 - W25


      --------------------------------------------------------------------------
     |PTY|ASRT |MON |________________________JUMPERS____________________________|                                             _______
     |LEV|     |    |18-19|19-20|21-22|22-23|24-25|25-26|27-28|28-29|30-31|31-32|
     |--------------------------------------------------------------------------|
     | 4*|  4  |5,6 | Out | In  | Out | In  | In  | Out | Out | In  | In  | Out |
     |--------------------------------------------------------------------------|
     | 5 | 4,5 | 6  | Out | In  | In  | Out | In  | Out | Out | In  | Out | In  |
     |--------------------------------------------------------------------------|
     | 6 | 4,6 | 7  | In  | Out | Out | In  | Out | In  | In  | Out | In  | Out |
     |--------------------------------------------------------------------------|
     | 7 |4,6,7|None| In  | Out | In  | Out | Out | In  | In  | Out | Out | In  |
     |--------------------------------------------------------------------------|
     |  *Factory Preset                                                         |
      --------------------------------------------------------------------------
 
                           Table 2-2:  Priority Level Configuration




                                            10






                                                        Factory Test
                   --------- 
                  \        /
                   \      /
                  ---------------------------++++++++++++++++++++++++---
                 |                           ||||||||||||||||||||||||   |
                 |                                               W35    |
                 |                           W1 W2 W3             *     |
                 |                           *  *  *     *  *  *  *     |
                 |                                      W44 45 33 34    |
                 |                                                      |
                 |                                                      |
                 |                                               W6     |
                 |                                               *      | Factory
                 |                                               W5     | Test
                 |                                               *      |
                 |                                               W4     |
                 |                                               *      |
                 |                                                      |
         22 Bit  |                   W7                                 |
         Address |                   *                                  |
                 |            W47 48 W8                                 |
                 |             *  *  *                                  |
                 |                   *                                  |
                 |                   W9                                 |  Address
                 |                                                      | Selection
         Step    |            W36 39                                    |
         Rate    |             *  *                                     |
                 |             *  *                                     |
                 |            W37 38                                    |
                 |                                                      |  Write
                 |                                                      | Precom-
         Boot-   |            W41        W15                            | pensation
         Strap   |             *          *                 *  *  *     |
                 |              *  *  *  *                 W14 13 12    |
                 |             W42 43 17 16                             |
                 |                                                      |
                 |                                   W20 19 18          |
                 |                 W10                *  *  *           | Interrupt
         TBS7    |                  *                 *  *  *           | Priority
                 |                  *                W23 22 21          |
                 |                 W11                                  |
                 |                                 W24 30 29            |
                 |                                  *  *  *             |
                 |                            _    W25 31 28            |
                 |_                        __| |    *  *  *            _|
                   |                      |    |    *  *  *           |
                   |                      |    |   W26 32 27          |
                    ----------------------      ---------------------

                            Figure 2-1:  Configuration Jumper Locations






                                            11






  2.1.3. Bootstrap         _________

         The controller board incorporates a transparent firmware bootstrap. 
         The bootstrap is initiated whenever program execution is started at
         location 173000U8D, homing all drives to track 0.  Next, track 1, sector
         1, of unit 0 is read and diskette density is determined.  If the
         diskette is single density, sectors 1, 3, 5, and 7 are loaded into
         memory starting at location 0. If the diskette is double density,
         sectors 1 and 3 are loaded.  Program execution is then transferred to
         location 0.  Controllers are shipped with this feature disabled.  To
         enable the bootstrap remove the jumper between W42 and W43 and insert
         the jumper between W41 and W42 as shown in Table 2-3.

                                  NOTE                                  ____

              Only one bootstrap should be enabled in a system for
              proper operation.  If another bootstrap exists in the
              system, it must be disabled before enabling the
              controller bootstrap.


                    --------------------------------------------------
                   |                   |           JUMPERS            |
                   |  BOOTSTRAP        |------------------------------|
                   |                   |     41-42     |     42-43    |
                   |--------------------------------------------------|
                   |  ENABLED          |       IN      |       OUT    |
                   |--------------------------------------------------|
                   |  DISABLED *       |       OUT     |       IN     |
                   |--------------------------------------------------|
                   |  *Factory Preset                                 |
                    --------------------------------------------------

 
                                   Table 2-3:  Bootstrap Option



  2.1.4. Write Precompensation         _____________________

         The MXV22 controller provides hardware write precompensation to reduce
         the bit shift exhibited by all drives as the recorded flux density
         increases.  The controller recognizes the patterns which produce bit
         shift and precompensates the written pattern.  This unique feature
         allows the controller to perform reliably with any Shugart compatible
         drive.












                                            12






         Controllers are shipped with this feature enabled and it is recommended
         that for more reliable operation the feature not be disabled.  However,
         if so desired, the feature can be defeated by cutting the foil-etched
         jumper between W12 and W13 and inserting a jumper between W13 and W14
         as shown in Table 2-4.


                    --------------------------------------------------
                   |                   |           JUMPERS            |
                   |      WRITE        |------------------------------|
                   |  PRECOMPENSATION  |     12-13     |     13-14    |
                   |--------------------------------------------------|
                   |  ENABLED*         |       IN      |       OUT    |
                   |--------------------------------------------------|
                   |  DISABLED         |       OUT     |       IN     |
                   |--------------------------------------------------|
                   |  *Factory Preset                                 |
                    --------------------------------------------------

                                 Table 2-4:  Write Precompensation


  2.1.5. Step Rate Control         _________________

         Up to four drives can be interfaced with the MXV22 controller.  These
         drives are organized into two pairs, each of which is associated with a
         particular register set.  The first pair of drives (DS1/DS2) is
         associated with the primary register set (177170U8D) and the remaining
         pair (DS3/DS4) with the secondary register set (177174U8D).  The
         controller is shipped configured with a 6ms step rate for both pair of
         drives.  Alternate step rates can be selected for each pair of drives. 
         Refer to Table 2-5 for desired step rate option and associated jumpers.


                    --------------------------------------------------
                   |   STEP RATE       |           JUMPERS            |
                   |-------------------|------------------------------|
                   | DS1/DS2 | DS3/DS4 |     36-37     |     38-39    |
                   |--------------------------------------------------|
                   |     6*  |    6*   |       IN      |       IN     |
                   |-------------------|---------------|--------------|
                   |     3   |    6    |       OUT     |       IN     |
                   |--------------------------------------------------|
                   |     6   |    3    |       IN      |       OUT    |
                   |-------------------|---------------|--------------|
                   |     3   |    3    |       OUT     |       OUT    |
                   |--------------------------------------------------|
                   |  *Factory Preset                                 |
                    --------------------------------------------------

                                       Table 2-5:  Step Rate






                                            13






  2.1.6. 22 Bit Addressing         _________________

         The controller is shipped with 22 bit addressing disabled.  Enabling
         this option provides extended address control during DMA transactions
         allowing the controller to transfer information throughout 22 bit
         address space.  The additional four bits of address (AU18D-AU21D) are
         communicated to the controller as described in section 3.1.2.  Before
         enabling this option it is necessary to modify the corresponding
         software drivers in order to maintain proper register communication as
         described in section 5.  To enable 22-bit addressing jumper W46 and W47
         as shown in Table 2-6.


                              -----------------------------------
                             |                   |    JUMPERS    |
                             |      22 BIT       |---------------|
                             |    ADDRESSING     |     46-47     |
                             |-------------------|---------------|
                             |  ENABLED          |       IN      |
                             |-------------------|---------------|
                             |  DISABLED *       |       OUT     |
                             |-----------------------------------|
                             |  *Factory Preset                  |
                              -----------------------------------

                                 Table 2-6:  22 Bit Addressing



  2.1.7. Miscellaneous Options         _____________________

         There are several options related to factory configuration of the
         controller.  These options must be configured as shown for proper
         operation of the controller.  Refer to Table 2-7 for these options. 
         During DMA operations if the bus address established extends into the
         peripheral address page the controller asserts bank select 7 (BS7) as
         required by normal bus protocol.  If the application requires extend
         memory overlapping the peripheral address page this option can be
         disabled as indicated in Table 2-7.


           ---------------------------------------------------------------------
         |   OPTION      |                       JUMPERS                        |
         |               |------------------------------------------------------|
         |               | 1-2  |  2-3  |  4-5  |  5-6  | 33-34 | 34-35 | 10-11 |
         |----------------------------------------------------------------------|
         |  FACTORY*     | OUT  |  IN   |  OUT  |  IN   |  OUT  |  IN   |   -   |
         |----------------------------------------------------------------------|
         |  BS7 ENABLED  |  -   |   -   |   -   |   -   |   -   |   -   |  IN   |
         |----------------------------------------------------------------------|
         |  BS7 DISABLED |  -   |   -   |   -   |   -   |   -   |   -   |  OUT  |
         |----------------------------------------------------------------------|
         |    * Factory Preset                                                  |
          ----------------------------------------------------------------------
                            Table 2-7:  Miscellaneous Options


                                            14







    2.2. DRIVE CONFIGURATION         ___________________

         The controller provides an industry standard floppy interface
         compatible with most available drives.  However, for proper operation,
         each drive must be configured with attention to several options. 
         Tables 2-8 thru 2-12 summarize these options for several of the more
         popular drives.

         --------------------------------------------------------------------
         |          |                            |       DUAL         SINGLE  |
         |  OPTION  |      DESCRIPTION           | DRIVE 0   DRIVE 1  DRIVE 0 |
         |--------------------------------------------------------------------|
         |   DS1    | Drive select 1             |   IN        OUT      IN    |
         |   DS2    | Drive select 2             |   OUT       IN       OUT   |
         |   DS3    | Drive select 3             |   OUT       OUT      OUT   |
         |   DS4    | Drive select 4             |   OUT       OUT      OUT   |
         |   A      | Radial head loading option |   IN        IN       IN    |
         |   B      | Radial head loading option |   IN        IN       IN    |
         |   C      | Head load option           |   IN        IN       IN    |
         |   D      | In use option              |   OUT       OUT      OUT   |
         |   X      | Radial head loading option |   OUT       OUT      OUT   |
         |   WP     | Inhibit write when protect |   IN        IN       IN    |
         |   NP     | Allow write when protect   |   OUT       OUT      OUT   |
         |   DS     | Stepper power from drive   |   IN        IN       IN    |
         |          | select                     |                            |
         |   HL     | Stepper power from head    |   OUT       OUT      OUT   |
         |          | load                       |                            |
         |   Z      | In use from drive select   |   OUT       OUT      OUT   |
         |   Y      | In use from head load      |   IN        IN       IN    |
         |   R      | Ready output               |   IN        IN       IN    |
         |   I      | Index output               |   IN        IN       IN    |
         |   DC     | Disk change output         |   X         X        X     |
         |   S      | Sector output              |   X         X        X     |
         |   800    | Sector option disable      |   IN        IN       IN    |
         |   801    | Sector option enable       |   OUT       OUT      OUT   |
         |   L      | -5V DC bias                |   IN        IN       IN    |
         |   T1     | Termination HL             |   OUT       IN       IN    |
         |   T2     | Termination drive select   |   IN        IN       IN    |
         |   T3     | Termination direction      |   OUT       IN       IN    |
         |   T4     | Termination step           |   OUT       IN       IN    |
         |   T5     | Termination write data     |   OUT       IN       IN    |
         |   T6     | Termination write gate     |   OUT       IN       IN    |
          --------------------------------------------------------------------

                          Table 2-8:  Shugart 801/851 Drive Configuration











                                            15






          ---------------------------------------------------------------------
         |           |                             |       DUAL        SINGLE  |
         |  OPTION   |      DESCRIPTION            | DRIVE 0  DRIVE 1  DRIVE 0 |
         |---------------------------------------------------------------------|
         |   U9      |Terminations for multiplexed |  IN        OUT      IN    |
         |           |inputs                       |                           |
         |   SI      |Internal write current switch|  X         X        X     |
         |   SE      |External write current switch|  X         X        X     |
         |   TR      |True ready output            |  IN        IN       IN    |
         |   RTR     |Radial true ready **         |  IN        IN       IN    |
         |   2S      |Two-sided status output*     |  IN        IN       IN    |
         |   DC      |Disk change option           |  OUT       OUT      OUT   |
         |   S1      |Side select option using     |  OUT       OUT      OUT   |
         |           |direction select *           |                           |
         |   S2      |Side select input *          |  IN        IN       IN    |
         |   S3      |Side select option using     |  OUT       OUT      OUT   |
         |           |drive select                 |                           |
         |1B,2B,3B,4B|Side select option using     |  OUT       OUT      OUT   |
         |           |drive select                 |                           |
         |   D       |Alternate input-in-use       |  OUT       OUT      OUT   |
         |   MS      |Motor on from drive select   |  IN        IN       IN    |
         |   MO      |Alternate input-motor-on     |  OUT       OUT      OUT   |
         |   MMO     |Alternate input-multiplexed  |  OUT       OUT      OUT   |         
         |           |motor on  **                 |                           |
         |   MD      |Motor off delay              |  IN        IN       IN    |
         |   R       |Ready output                 |  IN        IN       IN    |
         |   RR      |Radial ready                 |  IN        IN       IN    |
         |   SR      |Standard ready **            |  IN        IN       IN    |
         |   MT      |Modified true ready (outputs |  OUT       OUT      OUT   |         
         |           |true ready on pin 22)**      |                           |
         |   DS1     |Drive select 1               |  IN        OUT      IN    |
         |   DS2     |Drive select 2               |  OUT       IN       OUT   |
         |   DS3     |Drive select 3               |  OUT       OUT      OUT   |
         |   DS4     |Drive select 4               |  OUT       OUT      OUT   |
         |   Y       |Door lock/activity light     |  IN        IN       IN    |
         |           |activated from motor on **   |                           |
         |   Z       |Door lock/activity light     |  OUT       OUT      OUT   |
         |           |activated from drive select**|                           |
         |   PD      |Stepper power down           |  OUT       OUT      OUT   |
         |   WP      |Inhibit write when write     |  IN        IN       IN    |
         |           |protected                    |                           |
         |   NP      |Allow write when write       |  OUT       OUT      OUT   | 
         |           |protected                    |                           |
         |   TS      |Data separation option select|  OUT        OUT     OUT   |
          --------------------------------------------------------------------
         | X  Don't Care  * 860 Drive Only  ** Available on PCB Pin 25249 Only |         
         |                                                                     |
          ---------------------------------------------------------------------

                          Table 2-9:  Shugart 810/860 Drive Configuration







                                            16






          ----------------------------------------------------------------------
         |            |                             |       DUAL        SINGLE  |
         |   OPTION   |      DESCRIPTION            | DRIVE 0  DRIVE 1  DRIVE 0 |
         |----------------------------------------------------------------------|
         |   DS1      |Drive select 1               |  IN        OUT      IN    |
         |   DS2      |Drive select 2               |  OUT       IN       OUT   |
         |   DS3      |Drive select 3               |  OUT       OUT      OUT   |
         |   DS4      |Drive select 4               |  OUT       OUT      OUT   |
         |   A,B      |Radial head load             |  IN        IN       IN    |
         |   X        |Radial head load             |  OUT       OUT      OUT   |
         |   Z        |In use from drive select     |  OUT       OUT      OUT   |
         |   HL       |Stepper power from head load |  OUT       OUT      OUT   |
         |   R        |Alternate output ready pad   |  IN        IN       IN    |
         |   I        |Alternate output index pad   |  IN        IN       IN    |
         |   C        |Alternate input head load    |  IN        IN       IN    |
         |   D        |Alternate input-in-use       |  OUT       OUT      OUT   |
         |   DC       |Alternate output disk change |  OUT       OUT      OUT   |
         |   2S       |Alternate output 2-sided disk|  IN        IN       IN    |
         |   DS       |Stepper power from drive     |                           |
         |            | select                      |                           |
         |   Y        |In use from head load        |  IN        IN       IN    |
         |   DL       |Door lock latch              |  OUT       OUT      OUT   |
         |   RR       |Radial ready                 |  IN        IN       IN    |
         |   RI       |Radial index                 |  IN        IN       IN    |
         |   WP       |Inhibit write when write     |  IN        IN       IN    |
         |            |protect                      |                           |
         |   NP       |Allow write when write       |  OUT       OUT      OUT   |        
         |            |protect                      |                           |
         |D1,D2,D4,DDS|Drive address select         |  OUT       OUT      OUT   |
         |   B1-B4    |Two-sided drive select       |  OUT       OUT      OUT   |
         |   S1,S3    |Head select option           |  OUT       OUT      OUT   |
         |   S2       |Head select option           |  IN        IN       IN    |
         |   T40      |Test track 40                |  OUT       OUT      OUT   |
         |   HA       |Test actuate head load       |  OUT       OUT      OUT   |
         |4,6,8,10,12,|Alternate I/0 pins           |  OUT       OUT      OUT   |
         |16,18,24    |                             |                           |
          ---------------------------------------------------------------------

                             Table 2-10:  Qume 842 Drive Configuration


















                                            17






          ----------------------------------------------------------------------
         |            |                             |       DUAL        SINGLE  |
         |   OPTION   |      DESCRIPTION            | DRIVE 0  DRIVE 1  DRIVE 0 |
         |----------------------------------------------------------------------|
         |   DS1      |Drive select 1               |  IN        OUT      IN    |
         |   DS2      |Drive select 2               |  OUT       IN       OUT   |
         |   DS3      |Drive select 3               |  OUT       OUT      OUT   |
         |   DS4      |Drive select 4               |  OUT       OUT      OUT   |
         |   A,B      |Radial head load             |  IN        IN       IN    |
         |   X        |Radial head load             |  OUT       OUT      OUT   |
         |   Z        |In use from drive select     |  OUT       OUT      OUT   |
         |   HL       |Stepper power from head load |  OUT       OUT      OUT   |
         |   R        |Alternate output ready pad   |  IN        IN       IN    |
         |   I        |Alternate output index pad   |  IN        IN       IN    |
         |   C        |Alternate input head load    |  IN        IN       IN    |
         |   D        |Alternate input-in-use       |  OUT       OUT      OUT   |
         |   DC       |Alternate output disk change |  OUT       OUT      OUT   |
         |   2S       |Alternate output 2-sided disk|  IN        IN       IN    |
         |   Y        |In use from head load        |  IN        IN       IN    |        
         |   DL       |Door lock latch              |  OUT       OUT      OUT   |
         |   RR       |Radial ready                 |  IN        IN       IN    |
         |   RI       |Radial index                 |  IN        IN       IN    |
         |   WP       |Inhibit write when write     |  IN        IN       IN    |
         |            |protect                      |                           |
         |   NP       |Allow write when write       |  OUT       OUT      OUT   |        
         |            |protect                      |                           |
         |D1,D2,D4,DDS|Drive address select         |  OUT       OUT      OUT   |
         |   B1-B4    |Two-sided drive select       |  OUT       OUT      OUT   |
         |   S1,S3    |Head select option           |  OUT       OUT      OUT   |
         |   S2       |Head select option           |  IN        IN       IN    |
         |   T40      |Test track 40                |  OUT       OUT      OUT   |
         |   HA       |Test actuate head load       |  OUT       OUT      OUT   |
         |4,6,8,10,12,|Alternate I/0 pins           |  OUT       OUT      OUT   |
         |16,18,24    |                             |                           |
         |   SF       |Switch filter                |  IN        IN       IN    |  
         |   SP       |Stepper power (used with HL) |  OUT       OUT      OUT   | 
          ---------------------------------------------------------------------

                             Table 2-11:  Qume 242 Drive Configuration


















                                            18






          ------------------------------------------------------------------------
         |            |                               |       DUAL        SINGLE  |
         |   OPTION   |      DESCRIPTION              | DRIVE 0  DRIVE 1  DRIVE 0 |
         |------------------------------------------------------------------------|
         |   DS1      |Drive select 1                 |  IN        OUT      IN    |
         |   DS2      |Drive select 2                 |  OUT       IN       OUT   |
         |   DS3      |Drive select 3                 |  OUT       OUT      OUT   |
         |   DS4      |Drive select 4                 |  OUT       OUT      OUT   |
         |   Z        |In use from drive select       |  OUT       OUT      OUT   |
         |   R        |Alternate output ready pad     |  IN        IN       IN    |
         |   I        |Alternate output index pad     |  IN        IN       IN    |
         |   D        |Alternate input-in-use         |  OUT       OUT      OUT   |
         |   DC       |Alternate output disk change   |  OUT       OUT      OUT   |
         |   2S       |Alternate output 2-sided disk *|  IN        IN       IN    |
         |   DS       |Stepper power from drive       |  OUT       OUT      OUT   |    
         |            |select                         |                           |
         |   DL       |Diskette lever (optional)      |  OUT       OUT      OUT   |
         |   Y        |In use from head load          |  IN        IN       IN    |      
         |   HL       |Stepper power from head load   |  IN        IN       IN    | 
         |   C        |Head load option               |  IN        IN       IN    |
         |   RR       |Radial ready                   |  IN        IN       IN    |
         |   RM       |Ready modified                 |  OUT       OUT      OUT   |
         |   RI       |Radial index                   |  IN        IN       IN    |
         |   WP       |Inhibit write when write       |  IN        IN       IN    |
         |            |protected                      |                           |
         |   NP       |Allow write when write         |  OUT       OUT      OUT   |      
         |            |protected                      |                           |
         |   B1-B4    |Side select option using       |  OUT       OUT      OUT   |
         |            |drive select*                  |                           |
         |   S1       |Head select option             |  OUT       OUT      OUT   |
         |   S2       |Head select option             |  IN        IN       IN    |
         |   S3       |Head select option             |  OUT       OUT      OUT   |     
         |   M1       |Spindle motor option           |  IN        IN       IN    |
         |   M2       |Spindle motor option           |  OUT       OUT      OUT   |
         |   MC1-MC4  |Motor control select           |  OUT       OUT      OUT   |
         |------------------------------------------------------------------------|
         |     *  TM 848-2 Only                                                   | 
         |________________________________________________________________________|

                        Table 2-12 Tandon TM848-1/848-2 Drive Configuration

















                                            19







         2.2.1. Drive Selection Signals                _______________________

                The controller provides four radial drive select signals.  Each
                drive must be configured to one of the appropriate drive select
                signals.  Drive select 1 and drive select 2 (DS1/DS2) are
                associated with the primary register set (177170U8D) while drive
                select 3 and drive select 4 (DS3/DS4) are associated with the
                secondary register set (177174U8D).

                Upon initiation of a function the controller selects the
                appropriate drive, performs the operation and after ten
                revolutions of inactivity deselects the drive.


         2.2.2. Head Load Signal                ________________

                A separate head load signal is provided to prolong media life. 
                The read/write heads are only loaded on the media during
                read/write operations.  All other operations are completed with
                the heads in the unloaded position.

                Because step positioning can take place with the heads unloaded,
                the drive must be configured to provide stepper power
                independent of head loading.


         2.2.3. Motor Control                _____________

                The controller has been configured for ease of use with the
                newer DC motor drives.  A motor on signal is provided and is
                activated by the controller upon the initiation of any function.
                Before the drive is used for read/write operations, a motor
                delay timer insures the drive is up to speed.  After ten
                revolutions of inactivity, the signal is deselected, prolonging
                the life of the drive.

                The motor on delay timer has been configured to operate with
                drives jumpered with motor on as a function of drive select. 
                When a drive is selected the motor on signal is set.  If the
                motor on signal was previously set the drive ready status is
                immediately interrogated and if valid, the function is
                initiated.  If the drive is not ready a motor on delay is issued
                after which the drive ready status is again interrogated.  A
                valid ready status initiates the function while a not ready
                status results in a error being reported and the operation
                aborted.










                                            20





    2.3. CABLING         _______

         A 50-conductor ribbon cable connects to any Shugart compatible drive(s). 
         If the optional cable is purchased with the controller, connect the socket
         connector to the 50-pin header located at the edge of the controller
         board.  Observe the alignment of pin 1 of the socket connector and header
         as indicated by the arrows shown in Figure 2-2.  The two 50-pin connectors
         should be connected to the corresponding drives, again observing the
         location of pin 1.  If the optional cable is purchased from an independent
         source, the following list of materials (or equivalent) will help in the
         construction of the required cable.

              QTY        DESCRIPTION                  MFG        NUMBER              _________________________________________________________
              1 ea       50 pin socket connector      3M         3425-3000
              2 ea       50 pin edge connector        3M         3415-0001
              A/R        50 conductor ribbon cable    3M         3365/50

                                         Pin 1 ___
                                                  \ ___      ___      ___      ___
                                             ------|   |----|   |----|   |----|   |
                                            /      |   |    |   |    |   |    |   |
                                           /       |   |    |   |    |   |    |   |
                                          /--------|   |----|   |----|   |----|   |                                                    ___      ___      ___      ___
                                         \        \           \               
                                          \        \           \
                                           \        \            Card edge
                                            \        \           connector
                                             \        \          (50 pin)
                              Ribbon cable    \        \
                               (50 conductor)  \       |
                                                \      |
                                         /\      \     |
                                        /  \      \    |
                                       /    \    / \   |
                                      /      \  /   \  |
                                     /        \/     \ |
                                    / Pin 1___/       /
                                   /           \     /
                                  /             \   /    Socket
                                 /               \/\_____connector
                                /                   /      (50 pin)
                               /  Component Side   /
                              /                   /
                             /        MXV22      /
                             \                  /
                              \ B              /
                               \              /
                                \/\          /
                                  /         /
                                  \ A      /
                                   \      /
                                    \    /
                                     \  /
                                      \/
                          Figure 2-2:  Drive/Controller Cabling



                                            21






         The connector pins illustrated in Figure 2-3 are compatible with both
         the Shugart 800 series and 850 series drives.  Any drive that has both
         a Shugart compatible interface and connector should function properly
         with the controller.


                         -------       _______
                    ----| 1 | 2 |----->TG 43___                                       ________
                   |----| 3 | 4 |----->MOTOR ON
                   |----| 5 | 6 |
                   |----| 7 | 8 |      _________
                   |----| 9 |10 |<-----TWO SIDED
                   |----|11 |12 |      ___________
                   |----|13 |14 |----->SIDE SELECT
                   |----|15 |16 |      _________
                   |----|17 |18 |----->HEAD LOAD                                       _____
                   |----|19 |20 |<-----INDEX                                       _____
                   |----|21 |22 |<-----READY
                   |----|23 |24 |      ____________
                   |----|25 |26 |----->DRIVE SELECT 1                                       ______________
                   |----|27 |28 |----->DRIVE SELECT 2                                       ______________
                   |----|29 |30 |----->DRIVE SELECT 3                                       ______________
                   |----|31 |32 |----->DRIVE SELECT 4                                       ______________
                   |----|33 |34 |----->DIRECTION                                       ____
                   |----|35 |36 |----->STEP______                                       ____
                   |----|37 |38 |----->WRITE DATA                                       __________
                   |----|39 |40 |----->WRITE GATE                                       ________
                   |----|41 |42 |<-----TRACK 00_____                                       ________
                   |----|43 |44 |<-----WRITE PROTECT                                       _________
                   |----|45 |46 |<-----READ DATA
                   |----|47 |48 |
                   |----|49 |50 |
                   |     -------                   _
                   -

 
                              Figure 2-3:  Connector Pin Definitions


    2.4. CONTROLLER INSTALLATION         _______________________

         The controller  can be inserted and will function in any LSI-11 bus
         slot provided that both interrupt and DMA continuity are maintained. 
         Since these signals are daisy chained through the bus slots, no unused
         slots between LSI-11 processor and the floppy controller may exist. 
         Determine the order that the priority chain follows by consulting the
         documentation supplied with the LSI-11 system.  Note that when two
         interrupts of the same priority level are asserted, the closer a device
         is located to the processor, the higher its priority.









                                            22







    2.5. INITIAL OPERATION AND CHECKOUT         ______________________________

         Before the following procedures are done and for purposes of checkout,
         verify that the controller has been configured with two drives as
         described in Sections 2.1 - 2.4.

                                             NOTE                                             ____

                             The bootstrap must be disabled for
                             the following procedures.

    1.   Apply power to the drive(s).

    2.   Place the Run/Halt switch on the processor to the Halt position and
         turn on the processor.  An "@" character should be printed on the
         terminal signifying that console ODT has been entered.  Both drives
         (first drive 1, then drive 0) will step the heads inward 2-tracks, then
         step the heads outward until the home signal is detected.  The heads
         will not load.  If the above events do not occur, check the cabling and
         drive power supplies.

    3.  Place a preformatted scratch diskette in drive 0.                ____________

    4.  If the standard address assignment is selected, open the CS register
         using ODT by typing 177170/ on the terminal.  The processor will
         display the contents of the CS register.  If the controller is
         operating properly a 004040U8D should be printed.  Deposit a 40000U8D in
         the CS register by typing 40000 <CR>.  This command will initialize the
         controller.  Both drives should calibrate for home position.  First,
         drive 1 steps inward 2 tracks then outward one track at a time until
         the drive indicates track 0 has been reached.  The procedure is
         repeated on drive 0.  After both drives are calibrated, the head on
         drive 0 is loaded.  Sector 1 of track 1 on drive 0 is read into the
         controller buffer.  This operation is indicated by the in-use LED on
         the drive indicating the head load operation.  The LED will remain on
         for a short time after the read operation is complete.

         If, after initializing, the drives do not calibrate or the LED is not
         activated, check the cabling and power supplies.

    5.   Reopen the CS register (location 177170U8D) using ODT as described above.
         The contents of this location should be 004040U8D.  Examining the next
         location 177172U8D by using the line feed key or typing in 177172/ should
         yield either a 204U8D, 244U8D, 206U8D or 246U8D.  For a detailed description of
         the register protocol and bit definition, refer to Section 3.

    6.   If the above procedures function as described, the controller is ready
         for use.  Either diagnostics or an operating system can be booted.  For
         details on bootstrapping refer to Section 4.

    7.   If the above procedures cannot be validated, consult the factory or
         your local representative for assistance.




                                            23


          




























































                                            24













                                                                  SECTION 3


                                                                  FUNCTIONAL
                                                                  DESCRIPTION


      3. GENERAL         _______

         This section describes device registers and command protocol for the
         MXV22.

         All software control of the MXV22 is performed by means of two sets of
         two device registers:  the command and status (MXVCS) register and a
         multipurpose data buffer (MXVDB) register.  These registers are 
         assigned the bus address 177170U8D and 177172U8D, respectively, for the
         primary register set and 177174U8D and 177176U8D, respectively, for the
         secondary register set.  The registers can be read or loaded, with a
         few exceptions, using any instruction referring to their addresses.

         The MXVCS register passes control information from the CPU to the
         controller and reports status and error information from the controller
         to the CPU.  The MXVDB is provided for additional control and status
         information between the CPU and the controller.  The information that
         is present in the MXVDB at any given time is a function of the
         controller operation in progress.

         The controller contains a sector buffer capable of storing a complete
         sector.  For read/write operations the buffer is either "filled" before
         a write command or "emptied" after a read command under DMA control. 
         During a write command the controller locates the desired sector and
         the buffer information is transferred to the diskette.  During a read
         operation the desired sector is located and the sector data are
         transferred to the buffer.


    3.1. REGISTER DEFINITIONS         ____________________


  3.1.1. MXVCS - Command and Status Register (177170U8D or 177174U8D)         ___________________________________________U_D__________U_D_

         The format of the MXVCS register is shown below. Functions are
         initiated by loading the command and status (CS) register, when not
         busy (bit 5 = 1), with bit 0 = 1.  Command protocol is discussed in
         detail in Section 3.2.





                                            25





         15  14  13  12  11  10   9   8   7   6   5   4   3   2   1   0 
          ---------------------------------------------------------------
         |ERR|INT|EXT ADD|RX |   |HD |DEN|TR |INT|DN |UNT|  FUNCTION |GO |
         |   |   |       |02 |   |SEL|   |   |ENB|   |SEL|           |   |
          ---------------------------------------------------------------

         BIT DESCRIPTION         _______________

              15   ERROR:  This bit is set by the controller to indicate that an
                   error has occurred during an attempt to execute a command.
                   This bit is cleared by the initiation of a new command or by
                   setting the initialize bit.  When an error is detected the
                   MXVES is read into the MXVDB.  This bit is a read-only bit.

              14   MXV22 INITIALIZE:  This bit is set by the program to
                   initialize the controller without initializing all the
                   devices on the LSI-11 bus.  This is a write-only bit.

                                              CAUTION                                              _______
                             Loading the lower byte of the MXVCS will
                             also load the upper byte of the MXVCS.

                   When this bit is set, the controller will negate Done and
                   move the head position mechanism of drive 1 (if two drives
                   are available) to track 0.  When completed, the controller
                   will repeat the operation on drive 0.

                   The controller will then clear the error and status register,
                   set Initialize Done, and set Drive Ready if drive 0 is ready.
                   Finally, the controller will read sector 1, track 1, of drive
                   0.

           13-12   EXTENDED ADDRESS BITS:  These bits are used to specify an
                   extended bus address.  Bit 12 = MA16.  Bit 13 = MA17.  These
                   are write-only bits.

              11   RX02:  This bit is asserted by the controller to indicate
                   that this is an RX02 type system.  This is a read-only bit.

              10   RESERVED:  Must be written as a zero.

              09   HEAD SELECT:  This bit selects one of the two possible sides
                   of the disk for execution of the desired function.  When
                   cleared, side 0 is selected, when set, side 1 is selected. 
                   This is a read/write bit.

              08   DENSITY SELECT:  This bit selects either single or double
                   density operation.  When cleared, single density is selected;
                   when set, double density is selected.  This is a read/write
                   bit.

              07   TRANSFER REQUEST:  This bit signifies that the controller
                   needs data or has data available. This is a read-only bit.





                                            26





              06   INTERRUPT ENABLE:  This bit is set by the program to enable
                   an interrupt when the controller has completed an operation
                   and asserted the Done bit.  The condition of this bit is
                   cleared by initialize.  This is a read/write bit.

              05   DONE:  This bit indicates the completion of a function.  Done
                   will generate an interrupt when asserted if interrupt enable
                   (MXVCS bit 6) is set.  This is a read-only bit.

              04   UNIT SELECT:  This bit selects one of the two possible disks
                   for execution of the desired function.  This is a read/write
                   bit.

           03-01   FUNCTION SELECT:  These bits code one of the eight possible
                   functions described in detail within this section.  These are
                   write-only bits.

                        000   Fill Buffer
                        001   Empty Buffer
                        010   Write Sector
                        011   Read Sector
                        100   Set Media Density/Format
                        101   Read Status
                        110   Write Deleted Data Sector
                        111   Read Error Code

              00   GO:  Initiates a command (write-only bit).

  3.1.2. MXVDB - Data Buffer (177172U8D or 177176U8D)         ___________________________U_D__________U_D_

         This register serves as a general purpose data path between the
         controller and the LSI-11.  It will represent one of seven registers
         according to the protocol of the function in process.  These registers
         include the MXVDB, MXVTA, MXVSA, MXVWC, MXVBA, MXVBAE and MXVES.

         This register is a read/write register if the controller is not in the
         process of executing a command (i.e., it may be manipulated without
         affecting the controller).  When the controller is executing a command,
         the register can only be accessed when MXVCS bit 7 (TR) is set.

         Data Buffer Register (MXVDB)         ____________________________

         All information transferred to and from the floppy media passes through
         the MXVDB register and is addressable only under the protocol of the
         function in progress.

          15  14  13  12  11  10   9   8   7   6   5   4   3   2   1   0
          ---------------------------------------------------------------
         |   |   |   |   |   |   |   |   |   |   |   |   |   |   |   |   |
         |   |   |   |   |   |   |   |   |   |   |   |   |   |   |   |   |
          ---------------------------------------------------------------
         \---------------------------\/----------------------------------/
                                 READ/WRITE DATA

 
                                      MXVDB FORMAT



                                            27





         Track Address Register (MXVTA)         ______________________________

         This register is loaded to indicate on which of the 115U8D (77 decimal)
         tracks a given function is to operate.  It can be addressed only under
         the protocol of the function in progress.  Bits 8 through 15 are not
         used and are ignored.

          15  14  13  12  11  10   9   8   7   6   5   4   3   2   1   0 
          ---------------------------------------------------------------
         |///|///|///|///|///|///|///|///| 0 |   |   |   |   |   |   |   |
         |///|///|///|///|///|///|///|///|   |   |   |   |   |   |   |   |
          ---------------------------------------------------------------
         \---------------\/--------------/\--------------\/--------------/
                      NOT USED                         0-114U8D
 
                                      MXVTA FORMAT

         Sector Address Register (MXVSA)         _______________________________

         This register is loaded to indicate on which of the 32U8D (26 decimal)
         sectors a given function is to operate.  It can be addressed only under
         the protocol of the function in progress.  Bits 8 through 15 are not
         used and are ignored.

          15  14  13  12  11  10   9   8   7   6   5   4   3   2   1   0 
          ---------------------------------------------------------------
         |///|///|///|///|///|///|///|///| 0 | 0 | 0 |   |   |   |   |   |
         |///|///|///|///|///|///|///|///|   |   |   |   |   |   |   |   |
          ---------------------------------------------------------------
         \--------------\/---------------/\-------------\/---------------/
                     NOT USED                         1-32U8D
 
                                      MXVSA FORMAT

         Word Count Register (MXVWC)         ___________________________

         This register is loaded with the number of words (maximum of 128
         decimal) to be transferred.  At the end of each transfer the word count
         register is decremented.  When the contents of the register are
         decremented to zero transfers are terminated; Done is set (MXVES bit
         5);and, if enabled, an interrupt is requested.  If the word count is
         greater than the limit for the density specified, the controller
         asserts a Word Count Overflow (bit 10 of the MXVCS).  This register can
         be addressed only under the protocol of the function in progress.  Bits
         8 through 15 are not used and are ignored.

          15  14  13  12  11  10   9   8   7   6   5   4   3   2   1   0 
          ---------------------------------------------------------------
         |///|///|///|///|///|///|///|///|   |   |   |   |   |   |   |   |
         |///|///|///|///|///|///|///|///|   |   |   |   |   |   |   |   |
          ---------------------------------------------------------------
         \--------------\/---------------/\------------\/----------------/
                     NOT USED                        0-200U8D
 
                                      MXVWC FORMAT






                                            28






         Bus Address Register (MXVBA)         ____________________________

         This register is used to generate the bus address which specifies the
         location to and from which data are to be transferred.  The register is
         incremented after each transfer.  It will increment across 32K boundary
         lines via the extended address bits in the control and status register
         and the bus address extension register.  Systems with only 16 address
         bits will "wrap around" to location zero when the extended  address
         bits are incremented.  This register can be addressed only under the
         protocol of the function in progress.  Bit 0 is not used and is
         ignored.

          15  14  13  12  11  10   9   8   7   6   5   4   3   2   1   0 
          ---------------------------------------------------------------
         |   |   |   |   |   |   |   |   |   |   |   |   |   |   |   |///|
         |   |   |   |   |   |   |   |   |   |   |   |   |   |   |   |///|
          ---------------------------------------------------------------

 
                                      MXVBA FORMAT

         Bus Address Extension Register (MXVBAE)         _______________________________________

         This register contains the extended address bits (A18-A21) when 22 bit
         addressing is enabled.  Bits 4 thru 15 are not used and are ignored.

          15  14  13  12  11  10   9   8   7   6   5   4   3   2   1   0 
          ---------------------------------------------------------------
         |///|///|///|///|///|///|///|///|///|///|///|///|A21|A20|A19|A18|
         |///|///|///|///|///|///|///|///|///|///|///|///|   |   |   |   |
          ---------------------------------------------------------------

                                      MXVBAE FORMAT

         Error and Status Register (MXVES)         _________________________________

         This register contains the current error and status conditions of the
         drive selected by bit 4 (Unit Select) of the MXVCS.  This read-only
         register can be addressed only under the protocol of the function in
         progress.  The MXVES is loaded in the MXVDB upon completion of a
         function.

          15  14  13  12  11  10   9   8   7   6   5   4   3   2   1   0 
          ---------------------------------------------------------------
         |///|///|///|///|NXM|WC |HD |UNT|DRV|DD |DRV|DEN|AC |ID |SID|CRC|
         |///|///|///|///|   |OVF|SEL|SEL|RDY|   |DEN|ERR|LO |   |RDY|   |
          ---------------------------------------------------------------
         \------\/-------/
              NOT USED
 
                                      MXVES FORMAT








                                            29





         BIT DESCRIPTION         ___ ___________

         15-12   Not Used.

            11   NONEXISTENT MEMORY ERROR:  This bit is asserted by the
                 controller when the memory address specified for a DMA
                 operation is nonexistent.

            10   WORD COUNT OVERFLOW:  This bit indicates that the word count
                 specified is greater then the limit for the density selected. 
                 Upon detecting this error the controller terminates the fill or
                 empty buffer operation and asserts the Error and Done bits.

            09   HEAD SELECT:  This bit indicates the side currently selected. 
                 If cleared, it indicates drive 0; if set, it indicates side 1.

            08   UNIT SELECT:  This bit indicates the drive currently selected. 
                 If cleared, it indicates drive 0; if set, it indicates drive 1.

            07   DRIVE READY:  This bit is asserted if the unit currently
                 selected exists, is properly supplied with power, has a
                 diskette installed correctly, has its door closed, and has a
                 diskette up to speed.  This bit is only valid when retrieved
                 via a read status function or at the completion of initialize
                 when it indicates the status of drive 0.

            06   DELETED DATA:  During data recovery, the identification mark
                 preceding the data field was decoded as a deleted data mark.

            05   DRIVE DENSITY:  The bit indicates the density of the diskette
                 in the selected drive.  When zero, it indicates single density;
                 when set to one, it indicates double density.

            04   DENSITY ERROR:  A density error was detected as the information
                 was retrieved from the data field of the diskette (a density
                 error occurs when the density selected differs from that of the
                 data field).  Upon detecting this error the controller loads
                 the MXVES into the MXVDB and asserts the Error and Done bits.

            03   ACLO: Set by the controller to indicate a power failure.

            02   INITIALIZE DONE:  This bit is asserted to indicate completion
                 of the initialize routine, which can be caused by system power
                 failure, or programmable LSI-11 bus initialize.

            01   SIDE READY:  This bit is asserted by the controller when a
                 double-sided drive is selected, is ready, and has double-sided
                 media inserted.  The assertion of this bit indicates that side
                 1 of the selected drive is available for read and write
                 operations.

            00   CRC ERROR:  A cyclic redundancy check error was detected as
                 information was retrieved from a data field of the diskette. 
                 The information stored in the buffer should be considered
                 invalid.  Upon detection of this error the controller loads the
                 MXVES into the MXVDB and asserts the Error and Done bits.


                                            30






  3.1.3. Extended Status Registers         _________________________

         The controller has four internal status registers.  These registers
         provide specific error information in the form of error codes as well
         as drive status information depending upon the general error type.  The
         registers can be retrieved by a read error code function as described
         in Section 3.2.8.

         Word 1 <7:0> - Definitive Error Code         ____________________________________

         Octal Code Error Code Meaning         _____________________________

              040   Tried to access a track greater than 76.

              050   Home was found before desired track was reached.

              070   Desired sector could not be found after looking at 52
                    headers (2 revolutions).

              120   A preamble could not be found.

              150   The header track address of a good header does not compare
                    with the desired track.

              160   Too many tries for an IDAM (identifies header).

              170   Data AM not found in allotted time.

              200   CRC error on reading the sector from the disk.

              240   Density Error

              250   Wrong Key word for Set Media Density Command

              260   Illegal Data AM

              270   Invalid POK during write sequence

              300   Drive not ready.

              310   Drive write protected.

         Word 1 <15:8> - Not Used         ________________________

         This register is always cleared by the controller.

         Word 2 <7:0> - Current Track Address of Drive 0         _______________________________________________

         This register is cleared during the initialize command in order to
         synchronize with actual track position.  The register is updated with
         each seek on drive 0 and maintains current track position.






                                            31





         Word 2 <15:8> - Current Track Address of Drive 1         ________________________________________________

         This register is cleared during the initialize command in order to
         synchronize with actual track position.  The register is updated with
         each seek on drive 1 and maintains current track position.

         Word 3 <7:0> - Target Track of Current Disk Access         __________________________________________________

         If legal, the track specified for the last read/write command is saved
         in this register.

         Word 3 <15:8> - Target Sector of Current Disk Access         ____________________________________________________

         The sector specified for the last read/write command is saved in this
         register.

         Word 4 <15:8> - Track Address of Selected Drive         _______________________________________________

         This register contains the track address read from the sector header of
         the desired sector during the last read/write command.


    3.2. COMMAND PROTOCOL         ________________

         Data storage and recovery using the MXV22 controller is accomplished by
         careful manipulation of the MXVCS and MXVDB registers according to the
         strict protocol of the individual functions.  The penalty for violation
         of protocol can be permanent loss of data.  Each of the functions are
         encoded and written into the command and status register bits 1-3 as
         described in Section 3.1.1.  The detailed protocol for each function is
         described below.


  3.2.1. Fill Buffer (000)         _________________

         This function is used to fill the controller buffer with data from the
         host processor.  The number of words to transfer is specified by the
         host.  The command density bit determines the buffer size (64 or 128
         words).  The controller zero-fills the remaining buffer space.  If the
         word count is too large for the density selected, the function is
         aborted, Error and Done are asserted and the Word Count Overflow bit is
         set in the MXVES.

         The contents of the buffer may be written on the diskette with a
         subsequent write sector command or returned to the host processor using
         an empty buffer command.

         When the command is loaded, MXVCS bit 5 (Done) is negated.  MXVCS bit 8
         (density) must be set to define the buffer size.  MXVCS bits 12 and 13
         (extended address bits A16 and A17) must also be asserted to define the
         extended memory segment used with the buffer address, yet to be
         specified, to form the absolute memory address of the data to be
         transferred.  MXVCS bit 4 (unit select) and bit 9 (head select) are
         ignored since no drive operation is required.  When MXVCS bit 7 (TR) is
         first asserted, the program must move the word count into the MXVDB
         which will negate TR.


                                            32






         When the controller again asserts TR, the program must move the buffer
         address into the MXVDB.  If 22 bit addressing is enabled, the
         controller again asserts TR and the program must move the extended
         address bits (A18-A21) into the MXVDB.  The controller then negates TR,
         initiates a DMA cycle, and transfers the first word from the host
         processor to the controller buffer.  At the end of the transfer the
         word count register is decremented and the buffer address is
         incremented by two.  This cycle is repeated until the word count
         register becomes zero.  The controller zero-fills the remaining buffer
         space, sets the Done bit, and if enabled, causes an interrupt request. 
         After Done is asserted the MXVES is moved into the MXVDB.

         During the Data Transaction, if any non-existent memory is addressed,
         the controller will time out and abort the function.  The Error and
         Done bits will be asserted.  MXVES bit 11 (NXM) will be set and the
         MXVES will be moved into the MXVDB; if enabled, an interrupt request
         will be generated.


  3.2.2. Empty Buffer (001)         __________________

         This function is used to transfer the contents of the controller to the
         host processor.  The number of words to transfer is specified by the
         host.  The command density bit determines the maximum legal word count.
         If the word count specified is too large for the density selected the
         function is aborted, Error and Done are asserted and the Word Count
         Overflow bit is set in the MXVES.

         The contents of the buffer may be transfered to the host as many times
         as desired or may be written on the diskette with a subsequent write
         sector command.  Unless a fill buffer or read sector command is issued,
         the controller buffer is not destroyed.

         When the command is loaded, MXVCS bit 5 (Done) is negated, MXVCS bit 8
         (density) must be set to allow the proper word count limit.  MXVCS bits
         12 and 13 (extended address bits A16 and A17) must also be asserted to
         define the extended memory segment used with the buffer address, yet to
         be specified, to form the absolute memory destination address.  MXVCS
         bit 4 (unit select) and bit 9 (head select) are ignored since no drive
         operation is required.  When MXVCS bit 7 (TR) is first asserted the
         program must move the word count into the MXVDB which will negate TR. 
         When the controller again asserts TR the program must move the buffer
         address into the MXVDB.  If 22 bit addressing is enabled, the
         controller again asserts TR and the program must move the extended
         address bits (A18-A21) into the MXVDB.  The controller then negates TR,
         initiates a DMA, and transfers the first word of the buffer to the host
         processor.  At the end of the transfer, the word count register is
         decremented and the buffer address register is incremented by two. 
         This cycle is repeated until the word count register becomes zero.  The
         controller then sets the Done bit and if enabled causes an interrupt
         request.  After Done is asserted the MXVES is moved into the MXVDB.






                                            33





         During the DMA transaction, if any non-existent memory is addressed, 
         the controller will time out and abort the function.  The Error and
         Done bits will be asserted.  MXVES bit 11 (NXM) will be set and the
         MXVES will be moved into the MXVDB.  If enabled, an interrupt request
         will be generated.

  3.2.3. Write Sector (010)         __________________

         This function is used to locate a desired track and sector and write
         the sector with the contents of the internal sector buffer.  When the
         MXVCS is loaded with this command, the MXVES is cleared and both the TR
         and Done bits are negated.  When TR is first asserted the program must
         load the desired sector address into the MXVDB which will negate TR. 
         When TR is again asserted the program must load the desired track
         address into the MXVDB which will negate TR.  The controller then seeks
         the desired track and attempts to locate the desired sector.  The
         desired track is compared with the track field of the sector header. 
         If they do not match the operation is aborted, the Error and Done bits
         are asserted, the MXVES is moved into the MXVDB, and if enabled the
         controller will assert an interrupt request.

         If the densities agree but the controller is unable to locate the
         desired sector within two diskette revolutions, the controller will
         abort the operation, move the contents of MXVES into MXVDB, assert the
         Error and Done bits, and if enabled, assert an interrupt request.

         If the desired track and sector located and the densities agree, the
         controller will write the contents of the internal sector buffer
         followed by a CRC character, all in the function selected density.  The
         controller completes the operation by moving the MXVES to the MXVDB,
         asserts Done, and if enabled, asserts an interrupt request.

                                         CAUTION                                         _______

              The contents of the internal sector buffer are lost
              during a power failure.  However, after power is brought
              back to normal, a write sector command will cause the
              random contents of the buffer to be written on the
              diskette with a valid CRC character.

                                        NOTE                                        ____

              The contents of the sector buffer are not destroyed by a
              write sector operation.














                                            34






  3.2.4. Read Sector (011)         _________________

         This function is used to locate the desired track and sector and
         transfer the contents of the data field into the controller's internal
         sector buffer.  When the MXVCS is loaded with this command, the MXVES
         is cleared and both the TR and Done bits are negated.  When TR is first
         asserted the program must load the desired sector address into the
         MXVDB which will negate TR.  When TR is again asserted the program must
         load the desired track address into the MXVDB which will negate TR.

         Both the TR and Done bits remain negated while the controller attempts
         to locate the desired sector.  If after two revolutions the controller
         is unable to locate the desired sector, the operation is aborted.  The
         controller will move the MXVES into the MXVDB, assert the Error and
         Done bits, and if enabled, assert an interrupt request.

         When the desired sector is located, the controller will then compare
         the desired track with the track field of the sector header.  If they
         do not match, the operation is aborted.  The Error and Done bits are
         asserted, the MXVES is moved into the MXVDB, and if enabled, the
         controller asserts an interrupt request.

         If a legal data address mark is located and the densities of the
         diskette and function agree, the controller will read the data from the
         sector into the internal buffer.  If the data address mark indicated a
         deleted data field, MXVES bit 6 (DD) is set.  As data are stored in the
         internal buffer, a CRC is computed on the data and the CRC bytes
         recorded.  A non-zero result indicates a read error.  When a CRC error
         is encountered, the controller sets MXVES bit 0 (CRC), moves the MXVES
         into the MXVDB, asserts the Error and Done bits, and if enabled,
         asserts an interrupt request.

         If the desired sector is located, the density of the diskette and
         function agree, and the data are transferred with no CRC error, the
         controller will assert Done, and if enabled, will assert an interrupt
         request.


  3.2.5. Set Media Density (100)         _______________________

         This function is dual purpose.  The controller can set the media
         density by rewriting all the data address marks (single or double
         density) and writing zero data fields in the selected density.  The
         controller can also "reformat" the entire diskette by rewriting both
         the sector headers and the data fields.  The data fields are written in
         the selected density preceded by the corresponding data address mark. 
         Both commands are initiated by the set media function but differ in the
         keyword required by the controller to execute the command.









                                            35





         When the MXVCS is loaded with the command, the MXVES is cleared and the
         Done bit is negated.  When TR is set, the program must respond with a
         keyword.  This keyword must be deposited in the MXVDB to complete the
         protocol.  When the controller recognizes this character, it begins
         executing the command.  If an illegal keyword is used, the operation is
         aborted.  The MXVES is moved into the MXVDB, the Error and Done bits
         are set, and if enabled, the controller asserts an interrupt request.

         If the keyword used is a 111U8D, the controller initiates  a set media
         density operation.  This operation starts at track 0, sector 1.  Each
         sector header is located and a write operation is initiated.  A data
         field is written with zero data in the density selected.  If an error
         occurs reading any header, the operation is aborted.  The MXVES is
         moved into the MXVDB, the Error and Done bits are set, and if enabled,
         the controller asserts and interrupt request.  If the operation is
         successfully completed, Done is set and if enabled, the controller
         asserts an interrupt request.

         If the keyboard used is a 222U8D, the controller initiates a format
         operation.  This function starts at the physical index of track 0. 
         Each track is written first with an index address mark, then 26 sector
         headers are written sequentially about the track.  When each track has
         been written, the controller initiates a set media density function as
         described above.

         The following input string will format the selected unit, in the
         desired density.

                   777170/        4040        XXXX   <LF>                   _______                    ___________
                   177172/        000000      222    <CR>                                              ___________

 
                                    CAUTION 
                                    _______
              The set media density function takes about 15 seconds
              and the format function takes about 45 seconds.  Neither
              should be interrupted.  If either operation is
              interrupted, an illegal diskette has been generated, and
              the operation should be repeated.  If an error occurs
              during a set media density function or a format
              function, an illegal diskette has been generated.  The
              operation should be repeated. 


















                                            36






  3.2.6. Read Status (101)         _________________

         This function is used to update the drive status information and is
         initiated by loading the command into the MXVCS.  The Done bit is
         negated.  MXVES bit 7 (Drive Ready) is updated by sampling the drive
         ready status line.  Drive density is updated by loading the head of the
         selected drive and reading the first data address mark.  The controller
         then moves the MXVES into the MXVDB, asserts Done, and if enabled,
         asserts an interrupt request.  This operation requires about 250ms to
         complete.

 
                                          NOTE

                   If double-sided media are mounted in a double-sided
                   drive, MXVES bit 1 (side ready is set).


  3.2.7. Write Deleted Data Sector (110)         _______________________________

         This operation is identical to Write Sector (010) with one exception. 
         The data address mark preceding the data is not the standard data
         address mark.  A single or double density deleted data address mark is
         written according to the density of the function.


  3.2.8. Read Error Code (111)         _____________________

         This function is used to retrieve the extended status registers and is
         initiated by loading the MXVCS with the command.  The Done bit is
         negated.  When TR is asserted, the program must load the Bus Address
         into the MXVDB.  If 22 bit addressing is enabled, the controller again
         asserts TR and the program must move the extended address bits
         (A18-A21) into the MXVDB.  The controller then negates TR and assembles
         one word at a time and, under DMA control, transfers them to memory
         starting at the address specified.

         If non-existent memory is encountered during the transfer, the
         operation is aborted.  The Error and Done bits will be asserted, MXVES
         bit 11 (NXM) will be set, and the MXVES will be moved into the MXVDB. 
         If enabled, an interrupt request will be generated.

         When all four words have been transferred the Done bit is set and if
         enabled, an interrupt request is generated.














                                            37


          




























































                                            38














                                                                  SECTION 4


                                                                  CONTROLLER
                                                                  OPERATIONS


      4. GENERAL         _______

         This section provides the user pertinent information concerning the
         description and use of the controller functions.  The functions covered
         include:  bootstrapping, formatting, fill/write operations, read/empty
         operations, write current control, write precompensation, and power
         fail protection.


    4.1. BOOTSTRAPPING THE CONTROLLER         ____________________________

         If the bootstrap is enabled as described in Section 2.1.3, the
         controller will respond to the standard bootstrap address 173000U8D.  The
         controller is bootstrapped by typing 773000G while in console ODT. This
         causes a bus INIT and transfers program execution to location 173000U8D. 
         An alternate method is to strap the LSI-11 processor to power up Mode
         2.  In this mode, when a power up occurs, the processor automatically
         starts execution at 173000U8D.  Power-up strapping procedures for the
         LSI-11 processor can be found in the Microcomputer Processors
         Handbook.*

         To boot either a single or double density diskette use the following
         procedure:

              1.  Place the diskette in drive 0.

              2.  If the processor is strapped for power-up Mode 2,
                  operate the INIT (boot) switch or cycle DC power OFF
                  and ON.
              3.  If the processor is not strapped for power up Mode 2                                      ___
                  while in console ODT, type 773000G.








         *Published by Digital Equipment Corporation.  Maynard, Mass., 1979.


                                            39






  4.1.1. Bootstrap Operation         ___________________

         The bootstrap is not a standard ROM program.  It uses the controller's
         microprocessor to capture the bus; to read block 0 of the diskette into
         memory starting at location 0; and finally to transfer program
         execution to memory location 0.

         Any attempt to read location 173000U8D will result in a non-existent
         memory trap.  The controller only responds to this address immediately
         after a bus INIT.  For this reason the bootstrap is called
         "transparent".  When the processor attempts to fetch location 173000U8D
         following a bus INIT, the controller responds by passing the processor
         a "CLEAR RO" instruction.  The processor clears RO and then attempts to
         fetch location 173002U8D.  The controller passes the processor a "LOAD
         IMMEDIATE" instruction with R1 as the destination.  The processor then
         attempts to fetch the source operand from location 173004U8D. The
         controller passes the the device address 177170U8D if the standard
         address is selected, or 177174U8D if the alternate address is selected. 
         The processor moves the address into R1 and then attempts to fetch
         location 173006U8D.  The controller first asserts a Direct Memory Access
         Request (DMR) then passes the processor a "CLEAR PC" instruction. 
         Before the processor executes the instruction it passes bus mastership
         to the controller.  The controller moves a "BRANCH TO CURRENT LOCATION"
         instruction (777U8D) into memory location 0 under DMA control.  When the
         controller releases bus mastership the processor executes the "CLEAR
         PC" instruction and, in so doing, transfers program execution to
         location 0.  The processor is thus forced to loop at location 0.  The
         controller initiates a Read Status function on drive 0 to determine
         diskette density.  If the diskette is single density the controller
         reads sectors 1,3,5, and 7 of track 1 of drive 0 into locations 2
         through 176, 200 through 376, 400 through 576, and 600 through 776
         respectively.  If the diskette is double density the controller reads
         sectors 1 and 3 of track 1 of drive 0 into locations 2 through 376, and
         400 through 776 respectively.  Finally, the controller DMA's location 0
         with a NOP instruction (240U8D) allowing the processor to execute the
         system bootstrap.  If there is no diskette in drive 0 nothing will be
         transferred to memory and the processor will continue to loop at
         location 0 until halted.



    4.2. FORMAT OPERATIONS         _________________

         The controller has the capability of formatting diskettes in a
         specified density.  The formatting is accomplished in two passes. 
         During pass 1, an index address mark is written on track 0 following
         the index hole.  Twenty-six sector headers, appropriately spaced, are
         written following the index address.  Each of the remaining 76 tracks
         is written in the same manner.  When track 76 is completed, pass 2 is
         initiated.  The controller seeks track 0 and write a zero data field in
         sector 1 using the selected density.  The remaining sectors are written
         in the same manner.





                                            40





         The format command selects diskette density, unit and side (for dual
         headed drives).  Table 4-1 lists the various command word formats.

          -------------------------------------------------------
         |                          |   Unit 0     |   Unit 1    |
         |-------------------------------------------------------|
         | Single Density Side 0    |     11U8D      |     31U8D     |
         | Single Density Side 1    |   1011U8D      |   1031U8D     |
         | Double Density Side 0    |    411U8D      |    431U8D     |
         | Double Density Side 1    |   1411U8D      |   1431U8D     |
          -------------------------------------------------------

 
                            Table 4-1:  Command Word Formats

         Figure 4-1 illustrates a format subroutine.  The format command is
         loaded into MXVCS.  When TR is set, the keyword 222U8D is loaded into
         MXVDB.  When the diskette has been formatted a return is made.

         FORMAT:
                 MOV  #11, CMD          ;FORMAT
                 BIS  DENS, CMD         ;DENSITY
                 BIS  UNIT, CMD         ;UNIT
                 BIS  SIDE, CMD         ;SIDE
                 MOV  CMD, @#MXVCS      ;SELECT FUNCTION
                 JSR  PC, TRWAIT        ;WAIT FOR TR
                 MOV  #222, @#MXVDB     ;KEYWORD
                 JSR  PC, DNWAIT        ;WAIT FOR DONE
                 TST  @#MXVCS           ;ERROR
                 BMI  FRMERR            ;BR IF SO
                 RTS  PC
         FRMERR:

 
                             Figure 4-1:  Format Subroutine

         Alternatively a diskette can be formatted using console ODT.  Open the
         CS register and deposit the appropriate command.  Then deposit the
         format key word 222U8D in the DB register.  The following is an example
         of formatting unit 0 side 0 in double density.

         177170/       004040          411 <LF>         _______                       ________
         177172/       000000          222 <CR>                                       ________

















                                            41






    4.3. FILL/WRITE OPERATIONS         _____________________

         Figure 4-2 illustrates subroutines to write data on a diskette which is
         done by performing a fill buffer operation followed by a write sector.

         The Fill Buffer command, specifying single or double density is loaded
         into the MXVCS.  When TR is set, the word count is loaded into the
         MXVDB.  When TR is again set, the bus address of the data is loaded
         into the MXVDB.  If 22 bit addressing is enabled TR is again set and
         the extended address bits are moved into the MXVDB.  A return is made
         when the controller's sector buffer is filled.  The Write Sector
         command (specifying density, unit and side) is loaded into the MXVCS. 
         When TR is set the sector address is loaded into the MXVDB.  When TR is
         again set, the track address is loaded into the MXVDB.  When the
         contents of the controller's sector buffer are written at the selected
         sector, a return is made.

         FILLBF:
                 MOV     #1, CMD               ;FILL BUFFER
                 BIS     DENS, CMD             ;DENSITY
                 MOV     CMD, @#MXVCS          ;SELECT FUNCTION
                 JSR     PC, TRWAIT            ;WAIT FOR TR
                 MOV     COUNT, @#MXVDB        ;WORD COUNT
                 JSR     PC,TRWAIT
                 MOV     #BUFOUT, @#MXVDB      ;BUS ADDRESS OF DATA
                 JSR     PC, DNWAIT            ;WAIT FOR DONE
                 MOV     #EXTAD,@#MXVDB        ;EXTEND ADDR BITS*
                 JSR     PC, DNWAIT            ;WAIT FOR DONE*
                 TST     @#MXVCS               ;ERROR
                 BMI     ERFIL                 ;BR IF SO
                 RTS     PC
         ERFIL:

         WSECT:
                 MOV     #5, CMD               ;WRITE, SECTOR
                 BIS     DENS, CMD             ;DENSITY
                 BIS     UNIT, CMD             ;UNIT
                 BIS     SIDE, CMD             ;SIDE
                 MOV     CMD, @#MXVCS          ;SELECT FUNCTION
                 JSR     PC, TRWAIT            ;WAIT FOR TR
                 MOV     SECTOR, @#MXVDB       ;SECTOR
                 JSR     PC TRWAIT
                 MOV     TRACK @#MXVDB         ;TRACK
                 JSR     PC, DNWAIT            ;WAIT FOR DONE
                 TST     @#MXVCS               ;ERROR
                 BMI     WSERR                 ;BR IF SO
                 RTS     PC

         WSERR:

                 *only required if 22 bit addressing is enabled!

                               Figure 4-2:  Write Data Subroutines




                                            42






    4.4. READ/EMPTY OPERATIONS         _____________________

         Figure 4-3 illustrates subroutines to read data from a diskette which
         is done by performing a Read Sector operation followed by an Empty
         Buffer operation.

         The Read Sector command (specifying density, unit and side) is loaded
         into the MXVCS.  When TR is set the sector address is loaded into the
         MXVDB.  When TR is again set, the track address is loaded into the
         MXVDB.  When the contents of the selected sector are read into the
         controller's sector buffer, a return is made.

         The Empty Buffer command, specifying density, is loaded into the MXVCS.
         When TR is set, the word count is loaded into the MXVDB.  When TR is
         again set, the bus address of storage buffer is loaded into the MXVDB. 
         If 22 bit addressing is enabled TR is again asserted and the extension
         address bits are loaded into the MXVDB.  A return is made after the
         contents of the controller's buffer are transferred to the memory
         storage buffer.

         RSECT:  MOV     #7, CMD               ;READ SECTOR
                 BIS     DENS, CMD             ;DENSITY
                 BIS     UNIT, CMD             ;UNIT
                 BIS     SIDE, CMD             ;SIDE
                 MOV     CMD, @#MDVCS          ;SELECT FUNCTION
                 JSR     PC, TRWAIT            ;WAIT FOR TR
                 MOV     SECTOR, @#MDVDB       ;SECTOR
                 JSR     PC, TRWAIT
                 MOV     #EXTAD, @#MXVDB       ;EXTENDED ADDRESS BITS*
                 JSR     PC, DNWAIT            ;WAIT FOR DONE*
                 MOV     TRACK, @#MXVDB        ;TRACK
                 JSR     PC, DNWAIT            ;WAIT FOR DONE
                 TST     @#MXVCS               ;ERROR
                 BMI     RSERR                 ;BR IF SO
                 RTS     PC
         RSERR:

         EMPBF:  MOV     #3, CMD               ;EMPTY BUFFER
                 BIS     DENS, CMD             ;DENSITY
                 MOV     CMD, @#MXVCS          ;SELECT FUNCTION
                 JSR     PC, TRWAIT            ;WAIT FOR TR
                 MOV     COUNT, @#MXVDB        ;WORD COUNT
                 JSR     PC, TRWAIT
                 MOV     #BUFFIN, @#MXVDB      ;BUS ADDRESS FOR DATA
                 JSR     PC, DNWAIT            ;WAIT FOR DONE
                 TST     @#MXVCS               ;ERROR
                 BMI     EREMP                 ;BR IF SO
                 RTS     PC
         EREMP:

                 *only required if 22 bit addressing is enabled!

 
                               Figure 4-3:  Read Data Subroutines




                                            43






    4.5. WRITE CURRENT CONTROL         _____________________

         The controller provides a Write Current Control signal (TG43) which is
         asserted whenever a track address greater than 43 is accessed.  This
         signal is required by some drives to reduce the effects of write
         saturation on the inner tracks.  Since the Shugart 800 series drives do
         not require this signal, the controller is shipped with this feature
         disabled.  However, Shugart 850 series double sided drives require this
         signal (refer to the Shugart double sided diskette storage drive manual
         section 7.13).  This signal is provided on pin 2 of the 50 pin ribbon
         connector and is enabled according to section 2.1.4.

    4.6. WRITE PRECOMPENSATION         _____________________

         Bit shift occurs on both single and double density diskettes.  This
         shift is more noticeable with double density due to the smaller bit
         cell size and corresponding data and clock windows.  Some aspects of
         bit shift are predictable and are dealt with the precompensation scheme
         implemented in this controller; unpredictable effects are reduced by
         using PLL techniques.

         Predictable bit-shift effects result from normal read/write operation.
         Data are recorded by flux changes in the gap of the read/write head. 
         These flux changes produce changes in magnetization induces current in
         the read/write head.  Since this change is current is not
         instantaneous, it takes a finite time to build up to a peak and return
         to zero.  When the magnetic flux changes are close together the
         previous current transition may not reach zero before a second
         transition occurs.  The summation of current pulses produces shifted
         peaks.  Because the flux changes are closer together on the inner
         tracks (43 through 76) the bit shift is greater in this area.  Values
         of up to +350ns are typical.                  _

         Other causes of bit shift are variation disk drive rotational speed. 
         The specified +2% variation will produce bit shifts of +40ns.                        _                                        _
         Incomplete erasure of previously recorded data can produce bit shifts
         of up to 50ns.  Other miscellaneous components of bit shift include
         instantaneous speed variation, electrical noise, radial track alignment
         and nonsymmetry of the read/write head and associated electronics. 
         These effects can produce up to +10ns of bit shift, bringing the total                                         _
         effect to +450ns.                   _

         Since the data/clock window for double density is only 1000ns, a +450ns                                                                          _
         bit shift leaves only a 50ns margin before soft errors begin to occur. 
         To improve this margin the controller incorporates a scheme to
         recognize the data patterns which produce excessive bit shift and
         introduces a compensating bit shift.  For tracks greater than
         forty-three the recorded bits are shifted 165ns early, or late, as
         determined by the two previously recorded bits and the subsequent two
         bits to be recorded.  The controller also incorporates a phase-locked
         data recovery scheme which dynamically adjusts the recovery clock
         frequency to the data, reducing bit shifts due to rotational speed
         errors.  These two features improve data recovery margins by 175ns or
         more, providing approximately 225ns of margin.



                                            44






    4.7. POWER FAIL PROTECTION         _____________________

         The controller continuously monitors both the BPOK and BDCOK bus
         signals.  Refer to the Microcomputer Processors Handbook for detailed
         descriptions of these signals.  When asserted, BPOK signals an
         impending DC power failure and guarantees 4ms of operation before BDCOK
         is asserted and DC power fails.  Assertion of BDCOK indicates invalid
         DC power.  This signal is hardwired in the controller as an interlock
         on the Write Gate signal.  When BDCOK is asserted the Write Gate signal
         is blocked and write operations are prevented.

         Before initiating a write sequence, the controller interrogates the
         BPOK line.  If an impending DC failure is indicated the operation is
         aborted.











































                                            45


          




























































                                            46













                                                           SECTION 5


                                                           SOFTWARE
                                                           CONSIDERATIONS

      5. GENERAL         _______

         The MXV22 controller configured for 18-bit addressing can be used with
         all software designed to communicate with DEC's RXV21 controller.  This
         is of particular importance when using software not supported by the
         driver changes presented in this section.  This section describes the
         changes required to RT-11 and RSX-11M in order to take advantage of the
         22-bit DMA support provided by the MXV22 controller.  Once the changes
         described in this section have been incorporated into the applicable
         drivers the system software can be used with the MXV22 controller
         configured in either 18-bit or 22-bit modes.


                                         CAUTION

                   Operation via the MXV22 controller using unmodified
                   driver will yield questionable results if the MXV22
                   controller is configured for 22-bit addressing.



    5.1. OPERATION USING RT-11 V4.0         __________________________

         Operations involving the MXV22 controller are logically equivalent to
         those of the RXV21 except a modified "DY" driver is required when
         configured in 22-bit mode.  Several techniques can be used to
         incorporate the changes described in section 5.1.1; however, the
         changes can not be performed on the "DY" via the MXV22 controller
         without attention to the caution noted in section 5.

         The MXV22 (and RX02) controller requires a different handler than the
         single density controllers.  This new handler is configured to utilize
         the DMA transfer scheme of the controller.  In addition, diskette
         density is determined by the handler without system intervention,
         allowing the use of either single or double density diskettes
         interchangeably.

         This handler, designated "DY", is available in RT11-V03B and later
         revisions.





                                            47






         Although earlier versions of RT-11 can be used, only the changes to
         V4.0 are provided in this document.  Changes to earlier versions can be
         accomplished using the methodology described here and the judicial
         placement of similar code.  Earlier version will also require
         modification to the Bootstrap program BSTRAP


  5.1.1. Modifying RX02 Driver for RT11         ______________________________

         Changes listed in Appendix A are those required to modify DEC's V4.0
         RX02 driver for operation with the MXV22 controller.  Changes listed in
         Appendix A.1 are in a format expected by the Source Language Patch
         program (SLP).  Generate a file "DYMXV.DIF" using an editor of your
         choice containing changes listed in Appendix A.1.  Use the following
         steps to include the changes:

                   .RUN SLP
                   *DYMXV=DY,DYMXV


 
                                          NOTE

                   Changes in Appendix A are to edit level 2 of the
                   DY.MAC driver program.


         The file DYMXV.MAC will contain the new MXV22 compatible driver. 
         Assemble, link and install the new driver using the method described in
         your RT-11 System Generation Manual.


  5.1.2. Creating a DY-Compatible System Disk from a DX-based System         ___________________________________________________________

         The MXV22 controller requires the DY-based RT-11 monitor rather than
         the DX-based RT-11 monitor.  The following procedures explain how to
         create a DY-based system.

         Using an RX01 or equivalent system, or system which has an RX01 or
         equivalent peripheral device, the monitor file and other associated
         system files should be copied onto a single density diskette.  These
         files can be obtained from the binary distribution media or by
         performing a SYSGEN and specifying DY as the system device (refer to
         the RT11 System Generation Manual).  The following commands will
         initialize the diskette and copy the necessary files to Drive 1:

                             RT11V04

                   .INIT/NOQUERY DX1:
                   .COPY/SYS DEV:SWAP.SYS DX1:
                   .COPY/SYS DEV:RT11XX.SYS DX1:
                   .COPY/SYS DEV:TT.SYS DX1:
                   .COPY DEV:DIR.SAV DX1:
                   .COPY DEV:PIP.SAV DX1:
                   .COPY DEV:DUP.SAV DX1:



                                            48





         The bootstrap must then be copied from the monitor file to block 0 of
         the diskette.  The following command will accomplish this on the
         diskette in drive 1.

                                 RT11V04

                   .COPY/BOOT DX1:RT11XX DX1:

         This diskette can be used with the MXV22 controller but it is single
         density.  To build a double density diskette the user must first format
         a diskette to double density as explained in Section 4.2  Boot the
         single density system diskette in drive 0.  Use the following commands
         to initialize the formatted diskette in drive 1 and copy the system
         software from drive 0 to drive 1.

                                 RT11V04

                   .INIT/NOQUERY DY1:
                   .COPY/SYS DY:*.* DY1:

         Finally, copy the bootstrap to block 0 of the diskette in drive 1.

                                 RT11V04

                   .COPY/BOOT DY1:RT11XX DY1:

         The diskette in drive 1 can now be booted as a double density system
         diskette.


    5.2. OPERATION WITH RT-11 V5.0         _________________________

         Currently undefined.


    5.3. OPERATION WITH LAYERED PRODUCTS         _______________________________

         Using the driver modifications described for RT-11, layered products
         such as TSX-Plus V3.01, and SHARE 11 can be used to provide 22-bit
         system support with the MXV22 controller.


    5.4. OPERATION WITH RSX11M         _____________________

         Extended address support provided by the MXV22 controller is
         incorporated by the DYDRV changes listed in Appendix B.  An additional
         change is required to the device data I/O structure.  The file
         SYSTB.MAC created by Phase I of SYSGEN must be edited prior to assembly
         and task building process.  Characteristic word one of the Unit Control
         Block (UCB) must be edited to reflect 22-bit direct addressing support
         for the DYDRV device.  Refer to section 4 of the Guide to Writing and
         I/O Device for details.






                                            49







  5.4.1. Modifying RX02 Driver RSX11M         ____________________________

         Changes to the RX02 driver program DYDRV.MAC are provided in Appendix
         B.  The change are referenced to the distributed Version 2.13.  Changes
         listed in Appendix B are in the format expected by the Source Language
         Input Program (SLP).  These change can be incorporated into the
         standard driver using methods described in Section 17 of the RSX-11
         Utilities Manual.


    5.5. DOUBLE SIDED OPERATION RT-11/RSX-11M         ____________________________________

         Change for RT-11 double sided support is listed in Appendix A.2.  These
         changes can be used with the 22-bit changes.

         Appendix B.2 contain the changes required for RSX-11M double sided
         support.


    5.6. OPERATION WITH OTHER DEC SOFTWARE         _________________________________

         The MXV22 Controller used in 18-bit mode emulates the operation of the
         RXV21.  This is particularly important when using programs or systems
         that might require access to the RX02 type device.

 
                                          NOTE 
                                          ____

                   Operation of the XXDP Diagnostic program require
                   that the MXV22 be configured to emulate the RXV21
                   in 18-bit mode.


























                                            50













                                                                APPENDIX A.1


         The following changes are for incorporating 22-bit support via the
         Source Language Patch program (SLP):

         -/.IIF NDF DY$DD/,,/;MXV22/
         $22BIT = 1     ;Remove this line to disable 22-bit addressing
         .IIF NDF $22BIT, $22BIT = 0
         .IF NE $22BIT
         DYTYP=2000
         .ENDC
         -/@$MPPTR/+1,,/;MXV22/
         .IF EQ $22BIT
         -/BIS/,,/;MXV22/
         .IFF
                MOV     @SP,-(SP)
                ASL     @SP
                ASL     @SP
                MOV     (SP)+,EXMBIT
                SWAB    @SP
                BIC     #^C<30000>,@SP
                BIS     (SP)+,R4
         -/.ENDC/,,/;MXV22/
         .ENDC
         -/BUFRAD:/+3,,/;MXV22/
         .IF NE $22BIT
                BIT     #40000,R0       ;Boundary crossed?
                BEQ     8$              ;Branch if not
                INCB    EXMBIT
                BIC     #40000,R0       ;Remove bit
         -/.ENDC/,,/;MXV22/
         .ENDC
         -/DYDOFN:/+6,,/;MXV22/
         .IF NE $22BIT
                BIT     #DYTYP,@R4      ;Protocol complete
                BNE     3$
         2$:
         .ENDC
         -/RTS/,,/;MXV22/










                                            51





         .IF NE $22BIT
         3$:    MOV     R2,@R5
                MOVB    EXMBIT,R2
         4$:    BITB    #CSTR!CSDONE,@R4
                BEQ     4$
                BMI     2$
                JMP     DYERR2
                .BYTE   0
         EXMBIT:        .BYTE   0               ;Extended memory addr bits
         .ENDC
         -/8$:/+2,,/;MXV22/
         .IF NE $22BIT
                BIT     #DYTYP,@R4      ;22-bit controller?
                BEQ     22$             ;If equal no!
                CLRB    23$             
         22$:
         .ENDC
         -/MOV/,,/;MXV22/
         .IF NE $22BIT
         23$:   BR      9$
                JSR     PC,WAIT         ;One more transfer for 22-bit
                CLR     @R5
         .ENDC
         /


































                                            52














                                                                APPENDIX A.2


         The following changes are for incorporating double sided support for
         RT-11 via the Source Language Patch (SLP) program:

         -/.IIF NDF DY$DD/,,/;2SIDED/
         DY$DS=1
         MAXLSN=DYDSIZ*4
         DBSID2=2
         -/DOXFER:/,,/;2SIDED/
                MOV     DYLSN,R3
         -/DYLSN/,.,/;2SIDED/
         /



































                                            53














                                                                APPENDIX B.1


         The following changes are for incorporating 22-bit support for RSX-11M
         via Source Language Input Program (SLP):

         -/SDEN/,,/;MXV22/
         ADREXT =       2000            ; 22 BIT CONTROLLER BIT
         -/WD. 20/,,/;MXV22/
         ;      WD. 21 -- NOT USED
         -/(WD. 20)/,,/;MXV22/
         ;      I.PRM+16 (WD. 21) - EXTENDED ADDRESS BITS (BA18-BA21)
         -/SWAB/,.,/;MXV22/
                MOVB    UBUF(R5),R0     ; EXTENDED MEMORY BITS
                ROR     R0
                ROR     R0
                MOVB    R0,I.PRM+16(R1) ; SAVE BA18-BA21
                .REPT   3
                ROR     R0
                .ENDM
                BIC     #30000,R0       ; ISOLATE BA16 & BA17
                MOV     R0,UBUF(R5)     ; INITIALIZE CSR WORD
         -/280$:/+1,.,/;MXV22/
                CMPB    R0,#'I          ; END REGISTER PROTOCOL ?
                BEQ     284$            ; IF EQ EXIT
                BIT     #ADREXT,(R2)    ; 22-BIT CONTROLLER ?
                BEQ     284$            ; IF EQ YES
                MOV     R0,RXDB(R2)     ; LOAD TRACK, BUFFER ADDRESS, OR ASCII I
         281$:  BITB    #TR!DONE,(R2)   ; READY FOR LAST WORD ?
                BMI     283$            ; IF MI YES
                BEQ     281$
                BR      160$            ; ERROR, NO TRANSFER REQUEST
         283$:  MOV     I.PRM+16(R3),R0 ; EXTENDED ADDRESS BITS
         284$:  MOV     R0,RXDB(R2)     ; LOAD TRACK, BUFFER ADDRESS, OR ASCII I
         /














                                            54














                                                                APPENDIX B.2


         The following changes are for incorporating double sided support for
         RSX-11M  via Source Language Input Program (SLP):

         -/RSAE/,,/;2SIDED/
         SSIDED =       20000           ; SECOND SIDE INDICATOR BIT (U.CW2)
         -/CRCERR/,,/;2SIDED/
         SIDES  =       2               ; DOUBLE SIDED MEDIA
         -/220$:/,.,/;2SIDED/
         220$:  BIT     #SSIDED,U.CW2(R5) ; IS IT SECOND SIDE OPERATION?
                BEQ     225$            ; IF EQ NO
                BIS     #DSIDED,U.BUF(R5) ; USE SECOND SIDE
         225$:  MOVB    S.CON(R4),R1    ; RETRIEVE CONTROLLER INDEX
         -/440$:/,.,/;2SIDED/
         440$:  BIC     #SILO!SCHAR!SSIDED!ERR1,U.CW2(R5) ; CLEAR BITS
         -/470$:/,.,/;2SIDED/
         470$:  BIC     #SCHAR!DEN!DSIDED,U.CW2(R5) ; CLEAR FLAGS
         -/480$:/,.,/;2SIDED/
         480$:  BIT     #SIDES,I.PRM+6(R1) ; IS IT DOUBLE SIDED?
                BEQ     485$            ; IF EQ NO
                ASL     U.CW3(R5)       ; DOUBLE THE MAXIMUM LBN'S
                BIS     #DSIDED,U.CW2(R5) ; SET THE DOUBLE SIDED BIT
         485$:  MOV     #IS.SUC&377,R0  ; SET SUCCESS
         -/600$:/,.,/;2SIDED/
         600$:  BIT     #SIDES,I.PRM+6(R1) ; IS IT DOUBLE SIDED?
                BEQ     605$            ; IF EQ NO
                BIS     #DSIDED,U.CW2(R5) ; SET DOUBLE SIDED BIT
                ASL     U.CW3(R5)       ; DOUBLE MAX LBN'S
         605$:  MOV     R0,I.PRM+10(R1) ; STORE LOGICAL SECTOR NUMBER
         -/CMP  R0,#77./,/BEQ   60$/,/;2SIDED/
                CMP     R0,#76.         ; IS IT SECOND SIDE?
                BLT     30$             ; IF LT NO
                BITB    #IO.RPB&377,I.FCN(R3) ; PHYSICAL BLOCK FUNCTION?
                BEQ     23$             ; IF EQ NO, IT'S A LOGICAL BLOCK
                CMP     #76.,R0         ; YES
                BEQ     30$             ; IF EQ ALLOW ACCESS TO #76.
                SUB     #77.,R0         ; CHANGE SIDES - PHYBLK ACCESS
                BR      25$             ; CHANGE READ HEADS
         23$:   SUB     #76.,R0         ; ADJUST FOR SECOND SIDE
         25$:   BIT     #DSIDED,U.CW2(R5) ; TWO SIDE MEDIA?
                BEQ     60$             ; IF EQ NO, BAD BLOCK ERROR
                BIS     #SSIDED,U.CW2(R5) ; SET HEAD 1 SELECT BIT
         /




                                            55






                                     CONTENTS                                     ________


         PAGE         ____
         SECTION 1   GENERAL INFORMATION . . . . . . . . . . . . . . . . . . . 1
         COMPONENTS  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 2
         COMPATIBILITY . . . . . . . . . . . . . . . . . . . . . . . . . . . . 2
              Logical Track Format . . . . . . . . . . . . . . . . . . . . . . 3
              Sector Header Field  . . . . . . . . . . . . . . . . . . . . . . 4
              Data Field . . . . . . . . . . . . . . . . . . . . . . . . . . . 4
              Recording Scheme . . . . . . . . . . . . . . . . . . . . . . . . 5
              Double Frequency (FM)  . . . . . . . . . . . . . . . . . . . . . 6
              DEC Modified MFM . . . . . . . . . . . . . . . . . . . . . . . . 6
              Cyclic Redundancy Check  . . . . . . . . . . . . . . . . . . . . 7
         SPECIFICATIONS  . . . . . . . . . . . . . . . . . . . . . . . . . . . 7

         SECTION 2   INSTALLATION  . . . . . . . . . . . . . . . . . . . . . . 9
         GENERAL . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 9
         CONFIGURATION . . . . . . . . . . . . . . . . . . . . . . . . . . . . 9
         Address Vector Selection  . . . . . . . . . . . . . . . . . . . . . . 9
              Device Interrupt Priority  . . . . . . . . . . . . . . . . . .  10
              Bootstrap  . . . . . . . . . . . . . . . . . . . . . . . . . .  12
              Write Precompensation  . . . . . . . . . . . . . . . . . . . .  12
              Step Rate Control  . . . . . . . . . . . . . . . . . . . . . .  13
              22 Bit Addressing  . . . . . . . . . . . . . . . . . . . . . .  14
              Miscellaneous Options  . . . . . . . . . . . . . . . . . . . .  14
         DRIVE CONFIGURATION . . . . . . . . . . . . . . . . . . . . . . . .  15
              Drive Selection Signals  . . . . . . . . . . . . . . . . . . .  20
              Head Load Signal . . . . . . . . . . . . . . . . . . . . . . .  20
              Motor Control  . . . . . . . . . . . . . . . . . . . . . . . .  20
         CABLING . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  21
         CONTROLLER INSTALLATION . . . . . . . . . . . . . . . . . . . . . .  22
         INITIAL OPERATION AND CHECKOUT  . . . . . . . . . . . . . . . . . .  23

         SECTION 3   FUNCTIONAL DESCRIPTION  . . . . . . . . . . . . . . . .  25
         REGISTER DEFINITIONS  . . . . . . . . . . . . . . . . . . . . . . .  25
              MXVCS - Command and Status Register (177170U8D)  . . . . . . . .  25
              MXVDB - Data Buffer (177172U8D)  . . . . . . . . . . . . . . . .  27
              Extended Status Register . . . . . . . . . . . . . . . . . . .  31
         COMMAND PROTOCOL  . . . . . . . . . . . . . . . . . . . . . . . . .  32
              Fill Buffer (000)  . . . . . . . . . . . . . . . . . . . . . .  32
              Empty Buffer (001) . . . . . . . . . . . . . . . . . . . . . .  33
              Write Sector (010) . . . . . . . . . . . . . . . . . . . . . .  34
              Read Sector (011)  . . . . . . . . . . . . . . . . . . . . . .  35
              Set Media Density (100)  . . . . . . . . . . . . . . . . . . .  35
              Read Status (101)  . . . . . . . . . . . . . . . . . . . . . .  37
              Write Deleted Data Sector (110)  . . . . . . . . . . . . . . .  37
              Read Error Code (111)  . . . . . . . . . . . . . . . . . . . .  37

         SECTION 4   CONTROLLER OPERATIONS . . . . . . . . . . . . . . . . .  39
         GENERAL . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  39
         BOOTSTRAPPING THE CONTROLLER  . . . . . . . . . . . . . . . . . . .  39
              Bootstrap Operation  . . . . . . . . . . . . . . . . . . . . .  40

                                            i  


                                            





         FORMAT OPERATIONS . . . . . . . . . . . . . . . . . . . . . . . . .  40
         FILL/WRITE OPERATIONS . . . . . . . . . . . . . . . . . . . . . . .  42
         READ/EMPTY OPERATIONS . . . . . . . . . . . . . . . . . . . . . . .  43
         WRITE CURRENT CONTROL . . . . . . . . . . . . . . . . . . . . . . .  44
         WRITE PRECOMPENSATION . . . . . . . . . . . . . . . . . . . . . . .  44
         POWER FAIL PROTECTION . . . . . . . . . . . . . . . . . . . . . . .  45

         SECTION 5   SOFTWARE CONSIDERATIONS . . . . . . . . . . . . . . . .  47
         GENERAL . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  47
         OPERATION USING RT-11 V4.0  . . . . . . . . . . . . . . . . . . . .  47
              Modifying RX02 Driver for RT11 . . . . . . . . . . . . . . . .  48
              Creating a DY-Compatible System Disk from a DX-based System  .  48
         OPERATION WITH RT-11 V5.0 . . . . . . . . . . . . . . . . . . . . .  49
         OPERATION WITH LAYERED PRODUCTS . . . . . . . . . . . . . . . . . .  49
         OPERATION WITH RSX11M . . . . . . . . . . . . . . . . . . . . . . .  49
              Modifying RX02 Driver RSX11M . . . . . . . . . . . . . . . . .  50

         APPENDIX A  . . . . . . . . . . . . . . . . . . . . . . . . . . . .  51

         APPENDIX B  . . . . . . . . . . . . . . . . . . . . . . . . . . . .  54



































                                            ii