X-NEWS: eisner comp.music: 166
Relay-Version: VMS News - V6.1 30/1/93 VAX/VMS V5.5-2; site eisner.decus.org
Path: eisner.decus.org!noc.near.net!howland.reston.ans.net!europa.eng.gtefsd.com!uunet!news.tek.com!gvgpsa.gvg.tek.com!gvgspd.gvg.tek.com!not-for-mail
Newsgroups: comp.music
Subject: Re: MIDI Pin assignment
Message-ID: <24e2kc$n97@gvgspd.gvg.tek.com>
From: mrk@gvgspd.gvg.tek.com (Michael R. Kesti)
Date: 12 Aug 1993 11:37:00 -0700
References: <1993Aug11.195616.10539@ringer.cs.utsa.edu>
Distribution: inet
Organization: Grass Valley Group, Grass Valley, CA
Keywords: midi
NNTP-Posting-Host: gvgspd.gvg.tek.com
Lines: 112

In article <1993Aug11.195616.10539@ringer.cs.utsa.edu>
                             jkreth@lonestar.utsa.edu (Jeffrey A. Kreth) writes:

>Ok, we all know that midi only uses the bottom three pins on the standard
>DIN connector.

That's close enough.  The pin numbering is:

                              2
                          5       4
                        3           1


A typical tx/cable/rx circuit is:

           MIDI OUT port ---->|<- cable ->|<---- MIDI IN port             +5V
                                                          +5V        270   |
                 +5V        DIN           DIN              |     +--\/\/\/-+
                  |  220    +-+ +-------+ +-+   220    +-------+ |
             |\   +-\/\/\/--|4|-|-------|-|4|--\/\/\/--|2  8  6|-+--- UART RXD
             | \            | | |       | | |          | 6N138 |
 UART TXD ---|  \---\/\/\/--|5|-|-------|-|5|----------|3     5|-+
             |  /    220    | | +-------+ | |          +-------+ |
             | /         +--|2|-+       +-|2|                   GND
             |/ 7407     |  +-+           +-+
                        GND


>               What I would like to know is:
>
>What are the pin connections to hardwire a MIDI merge of different
>signals?  I've seen it done, but I don't remember the connections.

I doubt that what you have seen done implements a true merge.

MIDI is an asynchronous serial data protocol, much like RS-232 It uses an
oddball bit rate (compared to the RS-232 "standard" rates) and is a current
loop interface (rather than a voltage interface), but neither of these facts
is relevant to the following discussion.  This means that characters are
transmitted one bit at a time (serially!).  Also, many MIDI messages consist
of multiple characters.  For example, a Note On message is three bytes in
length: a Status (command) character, and two data characters that specify
which note, and velocity.

If one attempts to to merge two or more MIDI streams using a technique that
attempts merely to "mix" those two streams (which is, I think, what you are
suggesting), the temporal aspects of serial communications are bound to be
upset, because the two transmitters will eventually be transmitting
simultaneously.  This results in bit collisions that make it impossible to
determine whether a bit was a one or a zero, and the intermingling of
characters, which make it impossible to parse the received messages properly.
Many controllers send CLOCK and ACTIVE SENSING messages even when not being
played, so it doesn't help to add the caveat that you'll only play one
controller at a time.

To get around this, the true merger uses UARTs and a microprocessor.  The
usual scheme is to receive both streams store the received data in circular
buffers, and retransmit the data by extracting individual messages from the
buffers alternately.  This ensures that the bit and character order from
each stream is maintained, without the input streams appearing at the output
stream simultaneously.  Note that this does result in a delay through the
merger, but this can typically be held to a negligible amount.

What you may have seen is a switching scheme that allows one to determine
which of two MIDI outs are currently connected to a MIDI in.  The following
diagram and text comes courtesy of dale.eason@ncrnd3.stpaul.ncr.com (Dale
Eason):

                      2
                +--5     4--+
                | 3       1 |
                | MIDI IN B |
                |  +-----+  |
                |  |     |  |
                +--0     0--+         +------------------+
                   |     |            |                  |
      dpdt switch  0\    0------------+             2    |
                   | \---|---------------------- 5     4-+
                +--0     0--+                   3       1
                |  |     |  |                    MIDI OUT
                |  +-----+  |
                |           |
                |     2     |
                +--5     4--+
                  3       1
                  MIDI IN A

MIDI signals are on pins 4 and 5 of the midi connector. The connector
is numbered as shown above. Turning the switch connects either MIDI IN A or B
to coresponding pins 4 and 5 of the MIDI out connector.

The midi spec calls for the midi out jack to supply a ground for the shield
on pin 2, but only on the out device.  This shield helps prevent electrical
noise problems in the midi signal.  This swith does not do this but it
should be ok.  This means that the midi cable plugged into the Common MIDI
OUT jack will not have a shield attached to ground.  Try to keep that cable
as short a possible.  Long lines in an electrically noisey environment may
give you problems.  (An alternative would be to use a 3PDT switch, and
switch the grounds on pins 2 as well. - mrk)

A possible fix is to connect pin 2 from one of the MIDI IN's (MIDI IN A)
to the Common MIDI OUT pin 2.  Then make sure that you allways use MIDI IN A
if you only have one input connected.

Do not connect both of the MIDI IN pin 2's  together because it could cause
ground loop problems and will ruin the ground isolation between them.

-- 
============================================================================
Michael Kesti  Grass Valley Group, Inc. | "And like, one and one don't make
    mrk@gvgspd.GVG.TEK.COM              |  two, one and one make one."
    !tektronix!gvgpsa!gvgspd!mrk        |         - The Who, Bargain